## Slide 2
Meteor Lake (announced 19. 09.2023) – Intel’ first chiplet-based client proc.
(Intel 4 techn. four chiplets)

## Slide 3
Meteor Lake - 3D (Vertical) integration
Source: AnandTech 19. Sept- 2023

## Slide 4
Meteor Lake – first NPU (Neural Processing Unit) in Intel’s client processors

## Slide 5
Intel’s updated process evolution roadmap from 09/2023)
Source: AnandTech 19. Sept. 2023)

## Slide 6
Dezső Sima
Intel’s Core 2 family
Overview
September 2023
Vers. 4.1
© Dezső Sima 2023

## Slide 7
Intel’s Core 2 family - Overview
2. Overview of the evolution of Intel's Pentium 4 and
Core 2 families
3. Evolution of client (laptop and desktop) processors
4. Evolution of HEDT (High-End Desktop) processors
5. Evolution of high-end 2S server processors
6. Evolution of tablet- and smartphone processors
1. Introduction - Main battlefields of the processor war
7. References
Notes: 7

## Slide 8
1. Introduction - Main battlefields of the processor war
Notes: 8

## Slide 9: 1. Introduction - Main battlefields of the processor war (1)
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smarphones
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smartphones
Up to 64 C
Up to 32 C
Up to 10 C+ G
GPU less: Up to (8 + 16) C + G
With iGPU: Up to (8 + 16) C + G
Recent config.
1. Introduction - Main battlefields of the processor war
Major processor categories recently
Servers
Major processor categories recently
Clients
(Desktops/Laptops
HEDTs
(High-End Desktops)
Mobiles
(Tablets/Smartphones)
Remark: Usually, Intel and AMD designate their laptop processors as mobile processors,
by contrast, our Lecture classifies them as client processors.
This is because client processors (for laptops and DTs) are typically based on the x86 ISA,
whereas most mobile processors (for tablets and smartphones) are on the Arm ISA.

## Slide 10: 1. Introduction - Main battlefields of the processor war (2)
Who has recently faster processors Intel or AMD?
Image source: [43]

## Slide 11: 1. Introduction - Main battlefields of the processor war (3)
Main battlefields of the processor war
IC technology
Performance leadership
Accordingly, next, we summarize relevant developments in IC technology and
will show how Intel’s Core 2 and AMD’s Zen processors have been fighting for the
performance crone with alternating success.

## Slide 12: 1. Introduction - Main battlefields of the processor war (4)
Figure: Intel's lead in introducing new transistor technologies up to the 14 nm node [50]
a) The race in IC technology
Up to and including the 14 nm node (process technology) Intel lead the competition
in introducing new transistor manufacturing technologies by 2 to 4 years, as the
Figure below indicates.

## Slide 13: 1. Introduction - Main battlefields of the processor war (5)
Intel’s set back in developing the 10 nm technology, as indicated in lengthening
the cadence of their IC development cycle
2000
2002
2004
2006
2008
2010
2012
2014
2016
2018
200
180
160
140
120
100
80
60
40
0
20
180 nm
130 nm
90 nm
65 nm
45 nm
32 nm
22 nm
14 nm
10 nm
Pentium 4
Northwood
Pentium 4
Prescott
Pentium 4
Cedar Mill
Penryn
Westmere
Ivy Bridge
Broadwell
Pentium 4
Willamette
Cannon Lake
01/02
02/04
11/07
01/10
04/12
09/14
11/00
05/18
01/06
nm
≈ 3.5 years
Nevertheless, for switching from 14 nm to the 10 nm pilot production, Intel needed
almost 4 years, so experienced a setback in advancing IC technology, as seen
in the Figure above.
Meanwhile, the competition (TSMC, Samsung) caught up in IC development, moreover
overtook even Intel, as the following Figure shows.

## Slide 14: 1. Introduction - Main battlefields of the processor war (6)
TSMC’s recent lead in process technology vs. Intel [51]
Below we compare Intel’s and TSMC’s progress in IC manufacturing.
Table: Comparing Intel’s and TMSC’s nodes and their appearance [51]
Above Table indicates for each Intel process the equivalent (EN) TSMC’s process,
where “equivalent” means providing roughly the same transistor density (see also
the next Figure), and also similar frequency limits as well as power consumption.
As the Table shows, Intel began 10 nm mass production in 2019, this process
roughly equals TSMC’s 7 nm process, which already arrived one year earlier.
Similarly, Intel started mass production on the “Intel 7 node” in 2023, this process
is roughly the same as TSMC’s 3 nm riskc process, available since about 2021.

## Slide 15: 1. Introduction - Main battlefields of the processor war (7)
Comparing transistor densities (in 100 million transistors/mm2) of the same nodes
of major wafer foundries [47]
As the graph shows, Intel’s recent IC processes are roughly equivalent to TSMC’s or
Samsung’s next-generation IC processes, as far as transistor density is concerned.
E.g., Intel’s 10 nm technology provides approximately the same transistor density
as TSMC’s (Taiwan Semiconductor Manufacturing Company) or Samsung’s 7 nm process,
or Intel’s 7 nm technology approximately equals TSMC’s 5 nm or Samsung’s 3 nm process.
In order to accentuate this discrepancy, Intel introduced a new naming scheme of
their IC manufacturing processes (nodes) which deprives nm data, as follows:

## Slide 16: 1. Introduction - Main battlefields of the processor war (8)
Intel’s new process naming scheme from 07/2021 [52]
10 nm
Enhanced Superfin
7 nm
Previously
referred to
As the above Figure indicates, in the new naming scheme, Intel’s nodes have the same
designation (without the nm suffix) as TSMC’s roughly equivalent nodes, e.g., the
Intel7 node refers to a similar process as TSMC’s 7 nm node etc., (as indicated
in the previous Table).

## Slide 17: 1. Introduction - Main battlefields of the processor war (9)
Intel’s astonishingly dynamic process evolution roadmap, revealed in 12/2019 [12]
EUV: Extreme ultraviolet lithography
(Alder Lake
Raptor Lake)
(Meteor Lake)
The future will show whether Intel can fulfill the outlined very dynamic program.
?

## Slide 18: 1. Introduction - Main battlefields of the processor war (10)
Presented at AMD's Financial Analyst Day in May 16 2017
Flattening rise of clock frequencies while transistor technology evolves [13]

## Slide 19: 1. Introduction - Main battlefields of the processor war (11)
b) The race for the performance leadership -1
The dual-core Core 2 family brought Intel the performance leadership vs. AMD’s
also dual-core (Opteron-based) Athlon lines [53].
This has two reasons:
first, Intel had the better process technology (65 nm vs. 90 nm) and
second, Intel had wider cores, as Core 2-based processors had 4-wide- whereas
AMD’s K8-based processors only 3-wide cores.
Remark: Opteron was the name of AMD’s first 64-bit architecture that made use of
direct attached memory as well.

## Slide 20: 1. Introduction - Main battlefields of the processor war (12)
Figure: Example for Intel’s performance
leadership vs. AMD, it shows that
Intel’s Core 2 Duo E6750 provides
in all benchmarks higher
performance than AMD’s
Athlon 64X2 6000+ (except
in the Cinebench run) [54].
b) The race for performance
leadership -2

## Slide 21: 1. Introduction - Main battlefields of the processor war (13)
In the above Figure, AMD compares various performance metrics of their Zen 3-based
DT processors against Intel’s 10th gen. Core i9-10900K.
This announcement carried a strong marketing message since Intel touted its
previously released (04/2020) 10-core 10th gen. DT processor to be the best
gaming CPU available on the market. IPC: Instructions Per Cycle
AMD’s overtaking the performance leadership with their Zen 3-based processors
After nearly 15 years, in 11/2020, AMD claimed that their Zen 3-based gaming DTs
overtook the performance leadership over Intel’s 10th gen. DTs [46].

## Slide 22: 1. Introduction - Main battlefields of the processor war (14)
CineBench R20 Rendering benchmark Single Thread Scores |  |  |  | 
AnandTech | uArch | Process | 1C Turbo | Score
AMD Ryzen 9 5900X | Zen3 | TSMC 7nm | 4.8 GHz | 631pts
Intel Core i9-10900K | Comet Lake | Intel 14+++ | 5.0 GHz | 538pts
AMD Ryzen 9 3950X | Zen2 | TSMC 7nm | 4.7 GHz | 536pts
An example from the previous performance statements:
Single-thread Cynebench R20 scores of selected processors [46]
As the above data indicates, AMD’s Zen 3-based Ryzen 9 5900X has considerably
higher Cynebench R20 single-thread performance than Intel’s flagship
Core i9-10900K.
This mainly results from two facts;
at this time AMD had
a) the besser process technology (TSMC’s 7 nm vs. Intel’s 14+++ technology, and
b) a more efficient Zen 3 microarchitecture (albeit Intel enhanced their cores to
become 5-wide (beginning with their 6th gen. Tiger Lake line) whereas
AMD’s Zen cores remained still 4-wide.

## Slide 23: 1. Introduction - Main battlefields of the processor war (15)
Subsequent evolution of the processor performance battle Intel vs. AMD
Next, fierce competition has arisen between Intel’s and AMD’s comparable processors
where alternately, Intel and AMD overtook the performance leadership,
as the following Figure demonstrates.

## Slide 24: 1. Introduction - Main battlefields of the processor war (16)
17
19
18
22
21
05
04
06
07
2003
Alternating performance leadership in client processors AMD vs. Intel
A: AMD
I: Intel
CML: Comet Lake
ALL: Alder Lake
RPL: Raptor Lake
Year
2020
≈
*
A: Athlon 64
*
I: 10th gen. CML
*
I: Core 2
*
A: Zen 3 R 5000
*
I: 12th gen. ALL
*
A: Zen 4 R 7000
*
I: 13th gen. RPL
Performance
(not to scale)
Remark: The next 3 slides detail the performance results, they may be skipped.
R: Ryzen

## Slide 25: 1. Introduction - Main battlefields of the processor war (17)
The performance war: recent ranking of mobile processors (2021) -1
S: Snapdragon (Qualcomm)
E: Exynos (Samsung)
D: Dimensity (MediaTek)
GS101 (Google)
Performance/energy consumption of Apple’s, Qualcomm’s, /Samsung’s and MediaTek’s
processors [48]
Desktops

## Slide 26: 1. Introduction - Main battlefields of the processor war (18)
The performance war: recent ranking of mobile processors (2021) -2
As the cited results indicate, the big cores of Apple’s A14 and A15 processors
have an outstanding performance.
The next highest performance has Qualcomm’s X2 core, which is the Snapdragon 8 Gen1
processor’s big core.
Also, Qualcomm’s preceding big X1 cores of the Snapdragon 888 processors show
high performance, notably higher than Samsung’s or MediaTek’s A77 or
A78-based cores.
It is also worth noting that Apple’s big cores mentioned above perform already
at the level of Intel’s and AMD’s client processors, whereas they consume much
less power than client processors (with TDP values up to 100 W).

## Slide 27: 1. Introduction - Main battlefields of the processor war (19)
What’s next to expect from AMD and Intel concerning gaming DT processors?
Intel’s 14th gen. Meteor Lake DT processor (built on “Intel 4?” technology) is
expected to be launched in 2023.
AMD plans their Zen 5-based Granit Ridge DTs (based on 3 or 4 nm technology)
to be launched in 2023 or 2024, whereas
Thus, in the field of gaming DTs fierce competition is ahead between Intel and
AMD in the upcoming years.

## Slide 28: 1. Introduction - Main battlefields of the processor war (20)
The performance war: recent ranking of server processors (2021) -1
Per thread and SPECint2017 rate performance scores of Intel Xeon, AMD EPYC and
ARM-based (Amper Altra) server processors [49]

## Slide 29: 1. Introduction - Main battlefields of the processor war (21)
Note also in the previous Figure that lastly introduced Arm ISA-based server processors
already provide comparable performance levels as Intel’s and AMD’s current x86-based
server processors, though, typically consume less power and cost less.
The performance war: recent ranking of server processors (2021) -2
The previous Figure shows that in 2021, Intel’s 3rd gen. scalable Xeon 8380 provided
the highest ST performance, whereas AMD’s Zen 3-based EPYC 7763 has the highest
throughput while carrying out parallel workloads.
Nevertheless, this ranking might change when Intel or AMD will launch newer, more
enhanced server lines.
The lower power consumption of ARM-based servers mainly originates from the inherent
advantage of RISC type ARM ISAs vs. CISC type x86 ISAs.
This results from the fact that RISC architectures require less power for operand fetching
and decoding, since they fetch operands only from registers and decode fixed-length
instructions, whereas CISC processors may fetch memory operands as well and
decode variable length instructions.

## Slide 30
2. Overview of the evolution of Intel's Pentium 4 and
Core 2 families
2.1 Why Intel cancelled the Pentium 4 family?
2.2 Overview of the evolution of Intel's Core 2 family
2.3 What are the key enhancements of the Core 2 family?
Notes: 30

## Slide 31
2.1 Why Intel cancelled the Pentium 4 family?
Notes: 31

## Slide 32: 2.1 Why Intel cancelled the Pentium 4 family? (1)
The Netburst microarchitecture would have a lifespan of 7 years and its clock frequency
would break the 10 GHz mark in 2006 [4].
2.1 Why Intel cancelled the Pentium 4 family?
At the launch event of the Pentium 4 family (in Nov. 2000) Intel's vice president
(Otellini) introduced its underlying Netburst microarchitecture and made
the following promise:
What happened subsequently?

## Slide 33: 2.1 Why Intel cancelled the Pentium 4 family? (2)
01/2006
90nm
130nm
TICK TOCK
2 YEARS
2 YEARS
2 YEARS
65nm
TICK Pentium 4 (Cedar Mill SC)
Pentium D (Presler DC)
TOCK Core 2
2 YEARS
Pentium 4 /Northwood
TICK TOCK
TICK TOCK
Pentium 4 /Prescott
Pentium 4 /Willamette
07/2006
11/2000
01/2002
02/2004
180nm
Overview of the evolution of Intel's Pentium 4 family (Based on [5])
The Pentium 4 family has 3 generations, as follows: .
Note
The Pentium 4 had a single phase development model yet, as in each generation
Intel concurrently changed both the IC technology and the microarchitecture.

## Slide 34: 2.1 Why Intel cancelled the Pentium 4 family? (3)
Key new features of the ISA
and the microarchitecture
64-bit new microarch. ISA
Dual cores (DC) by dual dies
(Pentium D (Smithfield) (05/2005))
01/2006
90nm
130nm
TICK TOCK
2 YEARS
2 YEARS
2 YEARS
65nm
TICK Pentium 4 (Cedar Mill SC)
Pentium D (Presler DC)
TOCK Core 2
2 YEARS
New microarch.
called Netburst
New microarch.,
Hyperthreading (HT)
Pentium 4 /Northwood
TICK TOCK
TICK TOCK
Pentium 4 /Prescott
Pentium 4 /Willamette
07/2006
11/2000
01/2002
02/2004
180nm
What were the key innovations the Netburst microarchitecture introduced?

## Slide 35: 2.1 Why Intel cancelled the Pentium 4 family? (4)
Summing up: Key innovations of the Netburst microarchitecture and the ISA
During its lifetime, Intel introduced three key innovations into the Netburst microarchitecture
and the underlying ISA as follows:
hyperthreading (along with the 2. core (Northwood)) in 2002,
64-bit ISA and microarchitecture (along with the 3. core (Prescott)) in 2004 and
dual-core microarchitecture ((along with the 3. core (Prescott)) in 2005,
as has been indicated in the previous Figure.
Note
Dual-core Pentium 4 models were implemented by dual dies enclosed into the same
socket rather than integrating both cores on the same die (called monolithic integration).

## Slide 36: 2.1 Why Intel cancelled the Pentium 4 family? (5)
Overview of the Pentium 4 family -1
180 nm
130 nm
90 nm

## Slide 37: 2.1 Why Intel cancelled the Pentium 4 family? (6)
The previous Figure identifies three generations of Pentium 4 cores in different colors.
Furthermore, it indicates the introduction of hyperthreading in the 2. core by two
vertical lines, as well as the 64-bit extension of the 3. core by hatching in the model
designations.
Note that Intel has already implemented hyperthreading in their first launched
2. gen. DT cores, but announced its availability only along with the higher-priced
2. gen. server cores (this becomes obvious by looking at the transistor counts).
Similarly, Intel widened the 3. cores of the Pentium 4 family to 64-bit already in
the first launched 3. gen. DT cores but announced this extension (called EM64T)
only with the higher priced 3. gen. server cores (this becomes obvious again
by comparing the transistor counts).
In addition, this Figure also depicts the introduction of the low-performance
Celeron line in 2002 and the cancellation of certain high-speed 3. core models
in 2005.
Overview of the Pentium 4 family?

## Slide 38: 2.1 Why Intel cancelled the Pentium 4 family? (7)
Pentium 4
Pentium III
Pentium
≈ Limit of air cooling
For the related discussion see next slide.
The unexpected intense rise of dissipation in Intel's Pentium family -1

## Slide 39: 2.1 Why Intel cancelled the Pentium 4 family? (8)
The unexpected intense rise of dissipation in Intel's Pentium family -2
As the previous Figure shows, successive models of the Pentium family dissipated increasingly more power, the 3. core of the Pentium 4 family (called Prescott)
dissipated even nearly 100 W/cm2, a figure that equals roughly 100 W processor
dissipation, as its die measures approximately 1 cm2.
This steep rise of dissipation, however, could not be continued further on
since the resulting power dissipation would have become unmanageable high,
as absorbing 100 W dissipation by air cooling has already been a challenge
in DTs of that time.
As a consequence, overheating hindered Intel in achieving the announced 4 GHz
clock rate.

## Slide 40: 2.1 Why Intel cancelled the Pentium 4 family? (9)
Figure: In Oct. 2004, Crag Barrett, Intel's then-CEO, apologizes on his knees for
not have achieved the 4 GHz mark, in front of an audience of 7000 informatics professionals
at the IT Expo in Orlando [6]
Admitting Intel’s incapability to achieve 4 GHz in their Pentium 4 line
In Oct. 2004 Intel's CEO (Chief Executing Officer) admitted that the Pentium 4
family would not achieve even 4 GHz [6].

## Slide 41: 2.1 Why Intel cancelled the Pentium 4 family? (10)
Cancellation of announced high-frequency models due to overheating
180 nm
130 nm
90 nm

## Slide 42: 2.1 Why Intel cancelled the Pentium 4 family? (11)
Cancellation of the Pentium 4 line due to overheating
As the Pentium 4 line could not achieve its frequency targets, basically due to overheating,
it was withdrawn in 2005.

## Slide 43
Intel’s switch to a new processor design paradigm to cope with rising dissipation in 2003
Figure: Intel’s shift to a new design paradigm and revealing their IC manufacturing
and processor family roadmap at a shareholder’s meeting back in 4/2006 [7]
2.1 Why Intel cancelled the Pentium 4 family? (12)
Around 2003, Intel became aware of the seriousness of the overheating problem and shifted
the focus of their processor development from the pure performance target to the most
performance per watt goal, as stated in a slide from 4/2006 (see below).

## Slide 44
2.1 Why Intel cancelled the Pentium 4 family? (13)
Remark: A new design paradigm of processors invoked by the emergence of
mobile processors
High performance/power
(e.g. in GFLOPS/Watt)
Traditional processors
Tablets and smartphones
Low power
(in Watts)
(or in number of operating hours)
With the advent of mobile devices (about 2006), a new design paradigm arose as well,
as mobile devices require long operating hours i.e., low power consumption,
in sharp contrast to the design paradigm of traditional processors, as indicated below.

## Slide 45: 2.1 Why Intel cancelled the Pentium 4 family? (14)
In conceiving the Core 2 family why Intel fell back to a low power design?
Because dissipation led to the cancellation of the Pentium 4 family, Intel chose the
mobile-oriented Pentium M design as the starting point for developing the Core 2 family.

## Slide 46
2.2 Overview of the evolution of Intel's Core 2 family
2.21 What was Intel’s concept for developing subsequent
Core 2 generations?
2.2.2 How to categorize and name Core 2 processors?
2.2.3 What are the key enhancements of the Core 2 family?
Notes: 46

## Slide 47: 2.2 Overview of the evolution of Intel's Core 2 family (1)
2.2 Overview of the evolution of Intel's Core 2 family
Preliminary remarks
Intel launched their Core 2 family in 2006, and subsequently, for more than 10 years
Core 2-based processors lead the performance race and dominated the client and
server processor market.
Nevertheless, in the last few years, Core 2-based processors face a fierce competition
by AMD’s Zen-based and increasingly also by ARM ISA-based DT and server processors
(e.g. from Qualcomm, Ampere, or AWS).

## Slide 48
2.2.1 What was Intel’s concept for developing subsequent
Core 2 generations?
Notes: 48

## Slide 49: 2.2.1 What was Intel’s concept for developing subsequent Core 2 generations (1)
Along with the Core 2 family, Intel introduced a two-phase Tick-Tock model such that
yearly Tick and Tock phases follow each other, where
in the Tick phase, Intel basically reduces the feature size on the die, whereas
in the following Tock phase enhances the microarchitecture,
as the next Figure indicates it.
2.2.1 Intel’s concept for developing subsequent Core 2 generations? () 2.2.1 Intel’s concept for developing subsequent Core 2 generations? ()
2.2.1 What was Intel’s concept for developing subsequent Core 2 generations?

## Slide 50: 2.2.1 What was Intel’s concept for developing subsequent Core 2 generations (2)
The two phase processor development model introduced for the Core 2 family
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
(2006)
(2007)
(2008)
(2010)
(2011)
(2012)
(2013)
(2014)
Pentium 4
New
Process
65 nm
TICK
(2006)

## Slide 51: 2.2.1 What was Intel’s concept for developing subsequent Core 2 generations (3)
The two-phase approach aimed at reducing the vast complexity of developing
new processor architectures built on a new IC technology.
Why Intel introduced a two phase processor development model
for the Core 2 family
The two-year cycle between consecutive Tick phases obviously coincides with
Moore’s law.
A feature size reduction by 0.7 in the Tick phase allows
Notes
to implement the same number of transistors on ~ ½ Si die area or
to double the transistor count on about the same Si area.

## Slide 52: 2.2.1 What was Intel’s concept for developing subsequent Core 2 generations (4)
Intel’s stumbling in mastering the 10 nm technology -1
Intel maintained its more or less two-year-long development cycle from the
1. to the 6. gen. Core 2 processors while reducing the feature size from 65 nm
to 14 nm.
But mastering the subsequent 10 nm process caused Intel unexpected difficulties,
which lengthened the cadence of their processor development, as discussed next.
Originally, Intel planned to introduce the 10 nm technology already in 2015,
as their 2011 technology roadmap indicates [42] (see below).
By contrast, Intel’s 10 nm process became available only in 2018 as a pilot implementation
and even in 2019 for mass production, as the following Figure shows it for the
delayed introduction of the 10 nm pilot production.

## Slide 53: 2.2.1 What was Intel’s concept for developing subsequent Core 2 generations (5)
The last two technology transitions have signaled that our cadence today is closer
to 2.5 years than two“ [8].
In fact, Intel needed almost 4 years to master the 10 nm process.
Relating to their process difficulties Krzanich, Intel's CEO (Chief Executive Officer) told
at the earnings conference call of the firm on July 16 2015: “in the second half of 2017
we expect to launch our first 10-nanometer product, code named Cannon Lake.
2000
2002
2004
2006
2008
2010
2012
2014
2016
2018
200
180
160
140
120
100
80
60
40
0
20
180 nm
130 nm
90 nm
65 nm
45 nm
32 nm
22 nm
14 nm
10 nm
Pentium 4
Northwood
Pentium 4
Prescott
Pentium 4
Cedar Mill
Penryn
Westmere
Ivy Bridge
Broadwell
Pentium 4
Willamette
Cannon Lake
01/02
02/04
11/07
01/10
04/12
09/14
11/00
05/18
01/06
nm
≈ 3.5 years
Intel’s stumbling in mastering the 10 nm technology -2

## Slide 54: 2.2.1 What was Intel’s concept for developing subsequent Core 2 generations (6)
Leaving the two phase model and including additional “optimization” phases
after the Tock phase [9]
Figure: Intel’s switch to a new development model with
additional optimization phases included after the Tock phase [10]
To conceal the delay caused by difficulties in transitioning to the 10 nm process, Intel has
announced a new development model, including one or more optimization phases after
the Tock phase as well, as seen below.

## Slide 55: 2.2.1 What was Intel’s concept for developing subsequent Core 2 generations (7)
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TICK
TOCK
TICK
TOCK
TICK
TOCK
gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
(2006)
(2007)
(2008)
(2010)
(2011)
(2012)
(2013)
(2014)
Optimization phases introduced into the development model after the 6. generation
1. Introduction (1)
(2015)
(2016)
(2017/18)
Skylake
New
Microarch.
14 nm
TOCK
Optimization
6. gen.
Optimization
7. gen.
8. gen.1
Kaby Lake
New
Microarch.
14 nm
Kaby Lake R/G
Coffee Lake
Amber Lake-Y
Whiskey Lake-U
Cannon Lake (10 nm)
14 nm
Coffee Lake R
New
Microarch.
14 nm
Optimization
9. gen.
(2018)
R: Refresh
Kaby Lake Refresh
Kaby Lake G with AMD Vega
graphics
Coffee Lake
Amber Lake Y
Whiskey Lake U
(all 14 nm) and
Cannon Lake (10 nm)
1The 8th generation encompasses
the following processor lines:
Comet Lake
New
Microarch.
14 nm
Optimization
10. gen.
(2019)
lines [11].

## Slide 56: 2.2.1 What was Intel’s concept for developing subsequent Core 2 generations (8)
Note in the previous Figure that the 8th generation covers several new
families manufactured on Intel’s continuously enhanced still 14 nm process.
Surprisingly, among the mostly 14 nm 8th generation families, you will also find
Intel’s 10 nm Cannon Lake line that includes merely a dual-core GPU-less
low-power processor model.
The Cannon Lake line was announced in 05/2018 to demonstrate Intel’s 10 nm process
capability.
In fact, however, this line was only a pilot implementation; Intel needed about
one more year to mass produce 10 nm dies.
Remarks to the 8th generation

## Slide 57: 2.2.1 What was Intel’s concept for developing subsequent Core 2 generations (9)
Optimization cycle and backporting introduced after the 10th gen. Ice Lake line
Tiger
Lake
New
Microarch.
10 nm
Alder Lake
New Hybrid
Microarch.
10 nm
Optimization
New design
11. gen.
12. gen.
(2020)
(2021)
Ice
Lake
New
Microarch.
10 nm
TOCK
10. gen.
(2019)
Cannon
Lake
New
Process
10 nm
TICK
8. gen.
(2018)
Rocket Lake
New hybrid
Microarch.
14 nm
Back porting
11. gen.
(2021)
Intel’s first mass-produced 10 nm processors were the 10th gen. Ice Lake processors.
Next, Intel introduced the optimized 11th-gen. Tiger Lake line and subsequently also
the 11th gen. Rocket Lake line, which is a 14 nm backporting of the 10 nm 10th gen.
Ice Lake line with additional enhancements, not detailed here.
Note also that confusingly, both Intel’s 10 nm Ice Lake and 14 nm Rocket Lake lines
are named 11th generation processors (i.e., model designations begin in both
families by “11”).
Raptor Lake
New Hybrid
Microarch.
10 nm
Optimization
13. gen.
(2022)
Backporting

## Slide 58: 2.2.1 What was Intel’s concept for developing subsequent Core 2 generations (10)
Introducing a new hybrid (big.little) microarchitecture in the 12th generation
The 12th gen. Alder Lake line (2021) has an entirely new hybrid design that
incorporates up to 8 high-performance (P) and up to 8 high-efficiency (E) cores.
All announced models are client processors.
Tiger
Lake
New
Microarch.
10 nm
Optimization
New design
11. gen.
12. gen.
(2020)
(2021)
Ice
Lake
New
Microarch.
10 nm
TOCK
10. gen.
(2019)
Cannon
Lake
New
Process
10 nm
TICK
8. gen.
(2018)
Rocket Lake
New hybrid
Microarch.
14 nm
Back porting
11. gen.
(2021)
We point out that the Alder Lake line is not Intel’s first hybrid design since Intel
introduced already one year earlier the mobile-oriented multi-die Lakefield line
with 1 big and 4 little CPU cores.
Nevertheless, this line was not widely used even though it did not have a generation specifier.
The subsequent 13. gen. Raptor Lake line is an enhancement of the previous 12th
gen. Alder Lake line, it provides up to 8 P cores and up to 16 E cores.
Raptor Lake
New Hybrid
Microarch.
10 nm
13. gen.
(2022)
Alder
Lake
New Hybrid
Microarch.
10 nm
Optimization

## Slide 59: 2.2.1 What was Intel’s concept for developing subsequent Core 2 generations (11)
How much could Intel improve IPC in their Core 2 family up to the Ice Lake line [17] -1
Please note that the reference processor used is Intel’s Pentium M processor (Dothan), (2004).
(Core 2
(2006))
(Pentium M
(2004))
(2019)
IPC: Instructions Per Cycle

## Slide 60: 2.2.1 What was Intel’s concept for developing subsequent Core 2 generations (12)
How much could Intel improve IPC in their Core 2 family up to the Ice Lake line [17] -2
As the preceding Figure indicates, Intel achieved a more than twofold IPC increase
in their Core 2 family up to the 10th gen. Ice Lake line (in about 15 years).

## Slide 61
Basic µarchitectures | Basic µarchitectures and their shrinks and optimizations
Pentium 4 (Prescott) | 2005 90 nm Pentium 4 2006 65 nm Pentium 4
Core 2 | 2006 65 nm Core 2 2007 45 nm Penryn
Nehalem | 2008 45 nm Nehalem 2010 32 nm Westmere
Sandy Bridge | 2011 32 nm Sandy Bridge 2012 22 nm Ivy Bridge
Haswell | 2013 22 nm Haswell 2014 14 nm Broadwell
Skylake | 2015 14 nm Skylake 14 nm Kaby Lake 14 nm Coffee Lake 10 nm Cannon Lake
Ice Lake | 2019 10 nm Ice Lake 2020 10 nm Tiger Lake
Alder Lake | 2021 10 nm Alder Lake 2022 10 nm Raptor Lake
2.2.1 What was Intel’s concept for developing subsequent Core 2 generations (13)
Resulting new microarchitectures, their related shrinks and optimizations
Shown from Pentium 4’s 3rd core (Prescott) until the 13th gen. Raptor Lake line

## Slide 62: 2.2.1 What was Intel’s concept for developing subsequent Core 2 generations (14)
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
Haifa
Oregon
Oregon
Oregon
Haifa
Haifa
Oregon
Oregon
Intel’s design philosophy: running two competing design centers -1
1. Introduction (1)
Skylake
New
Microarch.
14 nm
TOCK
TOCK
6. gen.
TOCK
7. gen.
8. gen.1
Kaby Lake
New
Microarch.
14 nm
Kaby Lake R/G
Coffee Lake
Amber Lake-Y
Whiskey Lake-U
(Cannon Lake 10 nm)
14 nm
Coffee Lake R
New
Microarch.
14 nm
TOCK
9. gen.
R: Refresh
Kaby Lake Refresh
Kaby Lake G with AMD Vega
graphics
Coffee Lake
Amber Lake Y
Whiskey Lake U
(all 14 nm) and
Cannon Lake (10 nm)
1The 8th generation encompasses
the following processor lines:
Comet Lake
New
Microarch.
14 nm
TOCK
10. gen.
lines [11].
Haifa
Haifa
Haifa
Haifa
Haifa

## Slide 63: 2.2.1 What was Intel’s concept for developing subsequent Core 2 generations (15)
Intel’s design philosophy: running two competing design centers -2
Tiger
Lake
New
Microarch.
10 nm
Alder Lake
New Hybrid
Microarch.
10 nm
Optimization
New design
11. gen.
12. gen.
Ice
Lake
New
Microarch.
10 nm
TOCK
10. gen.
Cannon
Lake
New
Process
10 nm
TICK
8. gen.
Rocket Lake
New hybrid
Microarch.
14 nm
Back porting
11. gen.
Haifa
Haifa
Haifa
Haifa
Haifa
Raptor Lake
New Hybrid
Microarch.
10 nm
Optimization
13. gen.
Haifa
Remark
It seems curious why the Sandy Bridge family got the 2. gen. label.
This comes from the fact that Sandy Bridge was designed at Intel’s Haifa Design
Center where also the Core 2 family was developed, whereas the intermediate
Nehalem and Westmere families were designed at the Oregon Design Center.
Seemingly, while naming the Sandy Bridge family at Intel’s Haifa Design Center
, generations originating from elsewhere were left out.
?
Hybrid: big little architecture

## Slide 64
2.2.2 How to categorize and name Core 2 processors?
Notes: 64

## Slide 65: 2.2.2 How to categorize and name Core 2 processors? (1)
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smarphones
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smartphones
Up to 2x28 C
Up to 18 C
(Up to 10 C + G)
Up to 8 + 16 C + G
Recent config.
Remark: Intel usually designates their laptop processors as mobiles, as mentioned earlier.
Recent major processor categories and Intel’s related lines
Servers
Recent major processor categories and Intel’s related lines
Atom lines
Xeon E7/E5/E3
Platinum/Gold etc.
Clients
(Desktops/Laptops
Core i9/i7/i5/i3
(Basic architectures)
Atom lines
(+ LP Core models)
HEDTs
(High-End Desktops)
Core i7/i9
(Extreme Edition
or X models)
C a n c e l l e d i n 2 0 1 6
Mobiles
(Tablets/Smartphones)
2.2.2 How to categorize and name Core 2 processors?

## Slide 66: 2.2.2 How to categorize and name Core 2 processors? (2)
How Intel brandmarks their Core 2-based processors?
Client processors: marked by Core i3/i5/i7/i9 with various model name suffixes
HEDT processors: marked by Core i7/i9 with the model name suffixes E/EE/X/K
Server processors: marked by Xeon E3/E5/E7, where E refers to Enterprise.
Intel introduced the following branding conventions for their Core 2 processors:
Brandmark: Márkanév

## Slide 67: 2.2.2 How to categorize and name Core 2 processors? (3)
How Intel names their client processors? -1
Along with their Sandy Bridge family, Intel introduced a more or less standard
naming scheme that varies in client, HEDT, and server processors.
From these, below we discuss only Intel’s naming scheme of client processors,
by contrast, we do not outline the naming schemes of HEDT and server processors
as they have been changed multiple times, and their discussion would be rather
burdensome.

## Slide 68: 2.2.2 How to categorize and name Core 2 processors? (4)
How Intel named their client processors? -2
Figure: Naming scheme of client processors in Intel’s Core 2 family [14]
(Introduced along with the 2nd gen. Sandy Bridge line in 2011)
As an example the Figure below depicts the 7th gen. i7-7500U (Kaby Lake DT)
processor with the suffix U.
the first part is the brand modifier, which may be the i3/i5/i7/i9 label, followed
by a hyphen,
next comes the model number, which is 4 digits long up to the 9th generation
where the first digit identifies the generation, or
five digits long, beginning with the 10th generation, where the first two digits
identify the generation, finally, the third part is the
product line suffix, to be discussed later.
Until 2023 Intel’s client processors were named by Core brand name followed by
three name segments:

## Slide 69: 2.2.2 How to categorize and name Core 2 processors? (5)
Overview of the naming of Core 2-based client processors -1
1. Introduction (1)
Skylake
New
Microarch.
14 nm
TOCK
TOCK
6. gen.
TOCK
7. gen.
8. gen.1
Kaby Lake
New
Microarch.
14 nm
Kaby Lake R/G
Coffee Lake
Amber Lake-Y +R
Whiskey Lake-U
14 nm
Coffee Lake R
New
Microarch.
14 nm
TOCK
9. gen.
R: Refresh
Kaby Lake Refresh
Kaby Lake G with
AMD Vega graphics
Coffee Lake
Amber Lake Y
Whiskey Lake U
(all 14 nm) and
Cannon Lake (10 nm)
1The 8th generation
encompasses the following
processor lines:
Comet Lake
New
Microarch.
14 nm
TOCK
10. gen.
lines [11].
© Dezső Sima 2020
EE
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
i3/i5/i7--6xxx
-7xxx
-8xxx
(-10xxx for AL-Y R)
i3-i9-9xxx
i3-i9-10xxx
Clients
(2006)
(2007)
(2008)
(2010)
(2011)
(2012)
(2013)
(2014)
4/5/6xxx
-2xxx
-3xxx
-4xxx
-5xxx
i5/i7-xxx
i3/i5/i7-xxx
Clients
6/7/8/9xxx
(2015)
(2016)
(2017/18)
(2018)
(2019)

## Slide 70: 2.2.2 How to categorize and name Core 2 processors? (6)
Tiger
Lake
New
Microarch.
10 nm
Alder Lake
New Hybrid
Microarch.
10 nm
Optimization
New design
11. gen.
12. gen.
(2020)
(2021)
Ice
Lake
New
Microarch.
10 nm
TOCK
10. gen.
(2019)
Cannon
Lake
New
Process
10 nm
TICK
8. gen.
(2018)
Rocket Lake
New hybrid
Microarch.
14 nm
Back porting
11. gen.
(2021)
i3-8121U
Clients
i5-i9-11xxx
i3/i5/i7-10xxx
i3-i9-12xxx
i3-i9-11xxx
Raptor Lake
New Hybrid
Microarch.
10 nm
Optimization
13. gen.
(2022)
i5-i9-13xxx
Overview of the names of Core 2-based client processors -2

## Slide 71: 2.2.2 How to categorize and name Core 2 processors? (7)
Most frequently used client suffixes and related approximate TDP values:
Y: ultra low-power (11.5/13 W, SoC), when regular naming (i3/i5/i7-nxxxY) is used
or extreme low power (4.5/5 W SoC, when irregular naming m3/m5/m7-nYxx) is used
U: low power (typically 15/28 W, SoC)
H: high-performance mobile (typically 35/45 W)
Mobile suffixes (SoC: System on Chip)
Desktop suffixes
T – power-optimized models (ultra low power with 35/45 W TDP)
S – performance-optimized models (low power with 65 W TDP)
K – unlocked (adjustable CPU multiplier (60-95 W)
It is the last part of the model designations of client processors.
It refers to the TDP value of the processor, as indicated below.
Figure: Naming scheme of client processors in Intel’s Core 2 family [14]
(introduced along with the 2. gen. Sandy Bridge line in 2011)
The product line suffix of the names of Core 2-based client processors

## Slide 72: 2.2.2 How to categorize and name Core 2 processors? (8)
Intel’s renewed client naming scheme was introduced along with their 14th gen.
Meteor Lake line, introduced in 2023 [63]
After about 15 years, Intel modified their client processor’s naming schemes in three
aspects:
a) They dropped the “i” moniker from the model designations,
b) split off the “Core” brand into two sub-brands:
the mainstream-oriented “Intel Core” sub-brand with the brand-modifiers
3, 5 and 7, and
the premium category “Intel Core ULTRA” sub-branding with the brand modifiers
5, 7 and 9, as well as
c) placed the word “processor” between the brand-modifier and model number,
like Intel Core 5 processor ##xx, or Intel Core Ultra processor ##xx.

## Slide 73: 2.2.2 How to categorize and name Core 2 processors? (9)
Badges of the introduced “Intel Core” Ultra” and “Intel Core” sub-brands [63]

## Slide 74: 2.2.2 How to categorize and name Core 2 processors? (10)
Example die sizes of Intel’s 14 nm Core 2 processors (relative on scale) [18], [19]
Client dies
5th gen. Broadwell (2C, 82 mm2)
(with 5500 GPU)
Server die
6th gen. Skylake-SP (28C, ~680 mm2)
5th gen. Broadwell (2C, 133 mm2)
(with 6100/6200 GPU)

## Slide 75
2.2.3 What are the key enhancements of the Core 2 family?
Notes: 75

## Slide 76: 2.2.3 What are the key enhancements of the Core 2 family? (1)
Key enhancements of the Core 2 family
Key ISA extensions
Key enhancements of the microarchitecture
Key enhancements
to raise performance
Key enhancements
in power management
2.2.3 What are the key enhancements of the Core 2 family?
Overview

## Slide 77: 2.2.3 What are the key enhancements of the Core 2 family? (2)
a) Key ISA extensions of the Core 2 family (in client processors)
Key enhancements of the Core 2 family
Key ISA extensions
SIMD extensions
Key enhancements of the microarchitecture
128-bit FX (SSSE3)
128-bit FX/FP (SSE4)
256-bit FP (AVX)
256-bit FX/FP (AVX2)
512-bit FX/FP (AVX512)
Figure: Interpretation of
SIMD instructions [40]
X:
Y:
Z = X op Y
*
SIMD: Single Instruction Multiple Data

## Slide 78: 2.2.3 What are the key enhancements of the Core 2 family? (3)
PII
Klamath,
(1997)
Pentium_MMX
(1997)
Core
Cannon-Lake,
(2018)
Skylake-X/SP,
(2017)
(2016)
Evolution of Intel’s x86 ISA
extensions with pinpointing
the SIMD extensions [16]
FX
FX/FP
FP
FX/FP
FX/FP
Core 2

## Slide 79: 2.2.3 What are the key enhancements of the Core 2 family? (4)
Key enhancements
to raise performance
Key enhancements of the Core 2 family
Key enhancements
in power management
(see next Figure)
Key ISA extensions
SIMD extensions
(shown previously)
Key enhancements of the microarchitecture
b) Key enhancements of the microarchitecture
Subsection b) is not part of the test or the exam.
Its discussion aims at showing how intensely Intel developed the microarchitecture
of the Core line.

## Slide 80: 2.2.3 What are the key enhancements of the Core 2 family? (5)
Key enhancements of the Core 2 microarchitecture to raise performance
Key enhancements
to raise performance
Key enhancements of the Core 2 family
Key enhancements
in power management
(see next Figure)
Integrated memory controller
(NUMA architecture)
Integrated GPU
Private per-core L2 caches
with a shared L3 cache
Ring bus interconnect
Integrated PCIe controller
Raising the front-end width
of the cores (to 4/5/6)
Raising the back-end width
of the cores (from 5 to 17)
Raising the core count
(from 2 up to 16 in mobiles/DTs and
from 2 up to 56 in servers)
Key ISA extensions
SIMD extensions
(shown previously)
Key enhancements of the microarchitecture

## Slide 81: 2.2.3 What are the key enhancements of the Core 2 family? (6)
Main enhancements of the Core 2 microarchitecture to raise performance -1
Key new features of the ISA
and the microarchitecture
New microarch.: 4-wide core,
128-bit SIMD FX/FP EUs,
shared L2 , no HT
New microarch.: 256-bit (FP) AVX,
ring bus, integrated GPU
New microarch.: 256-bit (FX) AVX2,
L4 cache (discrete eDRAM), TSX
Shared Virtual Memory
In package integrated GPU
New microarch.: 4 cores, integr. MC,
QPI, private L2, (inclusive) L3, HT
New microarch.: 5-wide core,
ISP, Memory Side L4 cache, no FIVR
Optane memory, in KBL G series:
in package integr. CPU, GPU, HBM2
6C, (PCHs of S-series DTs support:
USB G2, integr. conn., Optane 2)
8C
2 YEARS
11/2007
01/2006
65nm
TICK Pentium 4 ( Cedar Mill)
Pentium D (Presler)
TOCK Core 2
07/2006
11/2008
01/2011
01/2010
32nm
45nm
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TOCK Haswell
04/2012
06/2013
09/2014
10/2015
14nm
6 YEARS
08/2016
08/2017
2 YEARS
10/2017
10/2018
TOCK Kaby Lake Refresh
TOCK Kaby Lake
TOCK Skylake
14nm
TICK Broadwell
TICK Ivy Bridge
2 YEARS
TOCK Coffee Lake Refresh
TOCK Coffee Lake
2G
3G
4G
5G
6G
7G
8G
8G
9G
1G
TOCK Comet Lake
10G
08/2019
TOCK Amber/Whiskey Lake
08/2018
8G
10C

## Slide 82: 2.2.3 What are the key enhancements of the Core 2 family? (7)
Key new features of the ISA
and the microarchitecture
New microarchitecture
Thunderbolt 3, WiFi 6
AVX 512
05/2018
07/2019
10nm
4 YEARS
TICK Cannon Lake
TOCK Ice Lake
TOCK Alder Lake
TOCK Tiger Lake
09/2020
11/2021
11G
12G
10G
8G
New big-little microarchitecture,
8+8 cores, 6-wide P cores
8+16 cores
2 YEARS
TICK Pentium 4 ( Cedar Mill)
Pentium D (Presler)
TOCK Core 2
Backporting to 14 nm
Rocket Lake
11G
14nm
03/2021
13G
10/2022?
TOCK Raptor Lake
Main enhancements of the Core 2 microarchitecture to raise performance -2

## Slide 83: 2.2.3 What are the key enhancements of the Core 2 family? (8)
Key enhancements
to reduce power consumption
Power gating
PCU (Power Control Unit)
FIVR (Fully Integrated Voltage Regulator)
Speed Shift Technology (CPPC)
Hybrid (big.little architecture)
Key enhancements to raise performance if there is a power/temperature headroom
Turbo Boost technology
Turbo Boost 2.0
Turbo Boost 3.0
Key enhancements in power management
Key enhancements of the microarchitecture concerning power management

## Slide 84: 2.2.3 What are the key enhancements of the Core 2 family? (9)
Main enhancements in power management of the Core 2 microarchitecture -1
2 YEARS
11/2007
01/2006
65nm
TICK Pentium 4 ( Cedar Mill)
Pentium D (Presler)
TOCK Core 2
07/2006
11/2008
01/2011
01/2010
32nm
45nm
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TOCK Haswell
04/2012
06/2013
09/2014
10/2015
14nm
6 YEARS
08/2016
08/2017
2 YEARS
10/2017
10/2018
TOCK Kaby Lake Refresh
TOCK Kaby Lake
TOCK Skylake
14nm
TICK Broadwell
TICK Ivy Bridge
2 YEARS
TOCK Coffee Lake Refresh
TOCK Coffee Lake
2G
3G
4G
5G
6G
7G
8G
8G
9G
1G
TOCK Comet Lake
10G
08/2019
TOCK Amber/Whiskey Lake
08/2018
Main enhancements
in power management
EDAT
Integrated Power Gates, PCU,
Turbo Boost
Turbo Boost 2.0
FIVR
2. gen. FIVR
Speed Shift Technology,
Duty Cycle control, No FIVR
except Skylake X
Speed Shift Technology v2
In H-series: TVB
(Thermal Velocity Boost)
STIM
Clock gating, PECI,
Platform Thermal Control by
3. party controller
8G

## Slide 85: 2.2.3 What are the key enhancements of the Core 2 family? (10)
Main enhancements
in power management
FIVR, Dynamic Tuning 2.0
(not discussed)
05/2018
07/2019
10nm
4 YEARS
TICK Cannon Lake
TOCK Ice Lake
TOCK Alder Lake
TOCK Tiger Lake
09/2020
11/2021
11G
12G
10G
8G
13G
10/2022?
TOCK Raptor Lake
Main enhancements in power management of the Core 2 microarchitecture -2

## Slide 86
3. Evolution of client (laptop and desktop) processors
3.1 Overview of Intel’s Core 2-based client processors
3.2 How have Intel’s Core 2-based client lines evolved
from their introduction in 2006 until now?
3.3 How was integrated graphics introduced and
has evolved in Intel’s Core 2 line?
Notes: 86

## Slide 87: 3. Evolution of client processors (1)
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smarphones
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smartphones
Desktops
Servers
Recent major processor categories of Intel
Xeon E7/E5/E3
Platinum/Gold etc.
Clients
(Desktops/Laptops)
Core i9/i7/i5/i3
(Basic architectures)
HEDTs
(High-End Desktops)
Core i7/i9
(Extreme Edition
or X models)
3. Evolution of client processors -1
Mobiles
(Tablets/Smartphones)
Atom lines
Atom lines
(+ LP Core models)

## Slide 88: 3. Evolution of client processors (2)
This Section is devoted to client processors, i.e., to processors that power desktops
and laptops.
First, we give an overview of the introduced generations of Core 2-based
client processors,
then we show how their key features, such as their core configurations, core count,
core width, memory speeds, and the way memory is attached to them
have evolved and finally
we briefly summarize the basics of graphics processing, as well as we discuss
how graphics processing has been integrated into the Core 2 line and how it
has evolved.
3. Evolution of client processors -2

## Slide 89
3.1 Overview of Intel’s Core 2-based client processors
Notes: 89

## Slide 90: 3.1 Overview of Intel’s Core 2-based client processors (1)
3.1 Overview of Intel’s Core 2-based client processors
Intel’s 64-bit Core 2 family is a continuation of the vendor’s former widely spread
processors, such as the 16-bit 8086, 8186, 80286, the 32-bit 80386, 80486,
Pentium, Pentium II, Pentium III and Pentium 4 lines.
We point out that the 80386 (1985) was Intel’s first 32-bit processor and the
Pentium 4 (2004) family was the last, as Intel performed the switch to 64-bit
along with the third core of this family.
By contrast, the Core 2 family, introduced in 2006, was from the beginning on a 64-bit
design.
The designation “client” processor came into use as the counterpart of the term
server processor, while client processors typically power laptops (notebooks)
and desktops (DTs).
Intel is introducing new Core 2-based client processor generations, usually yearly,
as shown in the following two Tables.

## Slide 91: 3.1 Overview of Intel’s Core 2-based client processors (2)
Gen. | Seg-ment | Attaching memory | Processor | Techno- logy | Max core count | Date of intro. | Socket | MCH/PCH | Mem. speed (up to) | Mem. channels
1. | M D | Attaching memory to the NB | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
 | D |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series | DDR3-1067 | 
 | D |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series | DDR3-1067 | 
 | D | Attaching memory to the processor die | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series | DDR3-1333 | 
 | M D |  | Westmere (M: Arrandale) D: Clarkdale/ | 32 nm | 2C+G | 1/2010 | M:BGA 1288 D:LGA 1156 | 5 Series |  | 
2. | M D |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | M: PGA 988 D: LGA 1155 | 6 series | DDR3-1333 | 
3. | M D |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 |  | 7 series | DDR3-1600 | 
4. | M D |  | Haswell | 22 nm | 4C+G | 6/2013 | M: BGA 1168 D: LGA 1150 | 8 Series | DDR3-1600 | 
4. | D |  | Haswell Refr. | 22 nm | 4C+G | 5/2014 |  | 9 Series | DDR3-1666 | 
5. | M D |  | Broadwell | 14 nm | 4C+G | 6/2015 |  | 9 Series | DDR3-1866 | 
 |  |  | Skylake | 14 nm | 4C+G | 10/2015 | M: BGA 1356 D: LGA 1151 | Series | DDR4-2133 | 
6. | M D |  |  |  |  |  |  |  |  | 
7. | M D |  | Kaby Lake | 14 nm | 4C + G | 8/2016 |  | 200 Series | DDR4-2400 | 
8. | M D |  | Coffee Lake | 14 nm | 6C +G | 10/2017 | M: BGA 1440 D: LGA 1151 | 300 Series | DDR4-2666 | 
8. | M |  | Amber Lake | 14 nm | 2C+G | 8/2018 | BGA 1515 | 300 Series | LPDDR3-2133 | 
8. | M |  | Whiskey Lake | 14 nm | 4C+G | 8/2018 | BGA 1528 | 300 Series | DDR4-2400 | 
9. | D |  |  |  |  |  |  |  |  | 
 |  |  | Coffee Lake R. | 14 nm | 8C +G | 10/2018 | LGA 1151 | 300 Series | DDR4-2666 | 
 |  |  | Comet Lake | 14 nm | 10C +G | 8/2019 | BGA 1528 LGA 1200 | 400 Series | DDR4-2666 | 
10. | M D |  |  |  |  |  |  |  |  | 
11. | D |  | Rocket Lake | 14 nm | 8C +G | 3/2021 | LGA 1200 | 400 Series | DDR4-3200 | 
Overview of Intel’s Core 2-based client generations -1

## Slide 92: 3.1 Overview of Intel’s Core 2-based client processors (3)
Gen. | Seg-ment | Attaching memory | Processor | Techno- logy | Max. core count | Date of intro. | Socket | PCH | Mem. speed (up to) | Mem. channels
8. | M | Attaching memory to the processor die | Cannon Lake | 10 nm | 2C | 5/2018 | BGA | n.a. | DDR4-2400 | 2
10. | M |  | Ice Lake | 10 nm | 4C+G | 7/2019 | Y: BGA 1377 U: BGA 1526 | 300-series | DDR4-3733 | 
11. | M D |  | Tiger Lake | 10 nm | 8C+G | 09/2020 | UP3: BGA 1449 UP4: BGA 1598 B/H: BGA 1787 | 400-series | LPDDR4x-4267 LPDDR5x-5400 | 
12. | M D |  | Alder Lake | 10 nm (Intel 7) | 8+8C+G | 11/2021 | M: BGA 1744 D: LGA 1700 | 600-series | DDR5-4800 | 4x 32-bit
13 | M D |  | Raptor Lake | 10 nm (Intel 7) | 8+16C+G | 09/2022 | LGA 1700 | 700-series | DDR5-5600 | 
Overview of Intel’s Core 2-based client processors -2

## Slide 93: 3.1 Overview of Intel’s Core 2-based client processors (4)
Recently, there has been fierce competition between Intel and AMD for processor
performance leadership in the client and server space.
This contest inspires both firms to aggressively enhance their processors' performance, this happens with alternating leadership.
What is the recent state of Intel’s Core 2-based client processors on the market?

## Slide 94: 3.1 Overview of Intel’s Core 2-based client processors (5)
To give an impression of recent client processors, below we show key features of
Intel’s high-performance 12th and 13th-gen. Core 2 models, while pointing out
that both families are already big.little designs.
Gen. | Seg-ment | Processor | Techno- logy | Max. core count | Date of intro. | Base fc GHz | Max Turbo fc (2 cores) GHz | Max Turbo fc (all cores) GHz | Base Power (TDP) | Max Turbo Power (all cores)
12. | M D | Alder Lake i9-12900KF | 10 nm (Intel 7) | 8P+8E+G | 11/2021 | P core: 3.20 E corer: 2.40 | 5.20 | 3.90 | 125 W | 241 W
13 | M D | Raptor Lake i9-13900KS | 10 nm (Intel 7) | 8P+16E+G | 09/2022 | P core: 3.20 E corer: 2.40 | 6.00 | 5.60 | 150 W | 320 W
Table: Clock rates and power consumption of Intel’s recent high-end big.little DT processors
Next, in Section 2.2 we discuss how key features of Core 2-based client lines evolved.
What are the key features of Intel’s current Core 2-based client processors?
As the above Table indicates, the depicted high-performance models of Intel’s 12th
and 13th gen. client processors achieve up to 3.2 GHz base- and 6.0 GHz
2-core turbo frequencies.
Nevertheless, such high clock rates should be paid for by high TDP values of 125 or
150 W, vs. typical, much lower TDP values of previous generations of up to 95 W.

## Slide 95
3.2 How have Intel’s Core 2-based client lines evolved
from their introduction in 2006 until now?
Notes: 95

## Slide 96: 3.2 How have Intel’s Core 2-based client lines evolved until now? (1)
3.2 How have Intel’s Core 2-based client lines evolved from their introduction
in 2006 until now?
The Core 2 Family is the most successful one in the history of processors owing
to its enormous evolution dynamics and a further aspects.
Subsequently, we only show how arbitrarily selected features have evolved, including
the core configuration (Section 3.2.1),
the core count (Section 3.2.2),
the core width (Section 3.2.3)
the way of attaching memory (Section 3.2.4),
the memory speed (3.2.5),
we also discuss how many memory channels are needed to serve more
and more CPU cores (Section 3.2.6) and
finally, we will be concerned with the introduction and evolution of
integrated graphics, due to its importance in a separate Section (Section 3.3).
Obviously, there are many more aspects that would be worth discussing,
e.g., advances in the ISA, cache architecture, interconnecting network, PCIe lanes,
power management, turbo technology, socketing, etc., but describing their striking
evolution would burst the frames of our Lecture.

## Slide 97: 3.2 How have Intel’s Core 2-based client lines evolved until now? (2)
3.2.1 How has the core configuration in Intel’s client processors evolved -1
Ring bus interconnect
Single core
CPUs
Core configurations of Intel’s client processors
Multicore CPUs
big.LITTLE
core clusters
Symmetrical
multicores
Dual core Pentium 4-based lines
(2005/2006)
1st - 11th gen.
Core 2-based lines
(2006-2020)
11th and 12th gen.
Core 2-based lines)
2021/2022)
Up to single core
Pentium 4-based lines
(up to 2004)
Ring bus interconnect
Intel has enhanced the core configuration of their client processors in three steps,
as shown below.

## Slide 98: 3.2 How have Intel’s Core 2-based client lines evolved until now? (3)
How has the core configuration in Intel’s client processors evolved -2
Obviously, Intel’s early client processors were single-core designs.
This changed when dual-core Pentium 4 processors appeared in 2004, yet implemented
on dual dies.
Next, monolithic multicore designs evolved with the introduction of the Core 2 family,
in 2006.
These designs are symmetrical multicores, where all cores are symmetrically
arranged and interconnected by a cache coherent interconnect, such as a ring bus.
Symmetrical multicores aim at raising performance by providing multiple cores.
In the last step of the evolution big.little (heterogeneous) designs appeared
along with the 12th gen. Alder Lake line (in 2021), where the microarchitecture
includes high-performance “big” cores and high-efficiency “little” cores.
Big.little architectures lower the power consumption by using the little, less
power-hungry cores for less demanding tasks.

## Slide 99: 3.2 How have Intel’s Core 2-based client lines evolved until now? (4)
3.2.2 How have CPU core counts raised?
Following advances in IC technology, Intel has already increased the maximum core
count of their Core 2-based client processors from 2 to 4 in 2007, and stuck at this
limit roughly for 10 years (as seen in the following Table), as most earlier applications
did not provide much more available parallelism.

## Slide 100
Raising max. core counts from 2 to 4 in Core 2-based client processors
3.2 How have Intel’s Core 2-based client lines evolved until now? (5)
Gen. | Seg-ment | Attaching memory | Processor | Techno- logy | Max core count | Date of intro. | Socket | MCH/PCH | Mem. speed (up to) | Mem. channels
1. | M D | Attaching memory to the NB | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
 | D |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series | DDR3-1067 | 
 | D |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series | DDR3-1067 | 
 | D | Attaching memory to the processor die | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series | DDR3-1333 | 
 | M D |  | Westmere (M: Arrandale) D: Clarkdale/ | 32 nm | 2C+G | 1/2010 | M:BGA 1288 D:LGA 1156 | 5 Series |  | 
2. | M D |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | M: PGA 988 D: LGA 1155 | 6 series | DDR3-1333 | 
3. | M D |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 |  | 7 series | DDR3-1600 | 
4. | M D |  | Haswell | 22 nm | 4C+G | 6/2013 | M: BGA 1168 D: LGA 1150 | 8 Series | DDR3-1600 | 
4. | D |  | Haswell Refr. | 22 nm | 4C+G | 5/2014 |  | 9 Series | DDR3-1666 | 
5. | M D |  | Broadwell | 14 nm | 4C+G | 6/2015 |  | 9 Series | DDR3-1866 | 
 |  |  | Skylake | 14 nm | 4C+G | 10/2015 | M: BGA 1356 D: LGA 1151 | Series | DDR4-2133 | 
6. | M D |  |  |  |  |  |  |  |  | 
7. | M D |  | Kaby Lake | 14 nm | 4C + G | 8/2016 |  | 200 Series | DDR4-2400 | 
8. | M D |  | Coffee Lake | 14 nm | 6C +G | 10/2017 | M: BGA 1440 D: LGA 1151 | 300 Series | DDR4-2666 | 
8. | M |  | Amber Lake | 14 nm | 2C+G | 8/2018 | BGA 1515 | 300 Series | LPDDR3-2133 | 
8. | M |  | Whiskey Lake | 14 nm | 4C+G | 8/2018 | BGA 1528 | 300 Series | DDR4-2400 | 
9. | D |  |  |  |  |  |  |  |  | 
 |  |  | Coffee Lake R. | 14 nm | 8C +G | 10/2018 | LGA 1151 | 300 Series | DDR4-2666 | 
 |  |  | Comet Lake | 14 nm | 10C +G | 8/2019 | BGA 1528 LGA 1200 | 400 Series | DDR4-2666 | 
10. | M D |  |  |  |  |  |  |  |  | 
11. | D |  | Rocket Lake | 14 nm | 8C +G | 3/2021 | LGA 1200 | 400 Series | DDR4-3200 | 

## Slide 101: 3.2 How have Intel’s Core 2-based client lines evolved until now? (6)
After AMD introduced Zen-based 8-core and 16-core (GPU-less) client processors
in 2017 and 2020, respectively, the processor market became competitive.
To encounter this challenge, Intel was forced to raise its core counts as well.
Accordingly, Intel launched first 6, then 8, and next 10-core client processors,
followed by even 16 and 24-core implementations in their big.little Alder Lake (2021)
and Raptor Lake (2022) families, as the following Tables show.
Raising max. core counts beyond 4 in Core 2-based client processors

## Slide 102
Raising max. core counts beyond 4 in Core 2-based client processors -2
3.2 How have Intel’s Core 2-based client lines evolved until now? (7)
Gen. | Seg-ment | Attaching memory | Processor | Techno- logy | Max core count | Date of intro. | Socket | MCH/PCH | Mem. speed (up to) | Mem. channels
1. | M D | Attaching memory to the NB | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
 | D |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series | DDR3-1067 | 
 | D |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series | DDR3-1067 | 
 | D | Attaching memory to the processor die | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series | DDR3-1333 | 
 | M D |  | Westmere (M: Arrandale) D: Clarkdale/ | 32 nm | 2C+G | 1/2010 | M:BGA 1288 D:LGA 1156 | 5 Series |  | 
2. | M D |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | M: PGA 988 D: LGA 1155 | 6 series | DDR3-1333 | 
3. | M D |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 |  | 7 series | DDR3-1600 | 
4. | M D |  | Haswell | 22 nm | 4C+G | 6/2013 | M: BGA 1168 D: LGA 1150 | 8 Series | DDR3-1600 | 
4. | D |  | Haswell Refr. | 22 nm | 4C+G | 5/2014 |  | 9 Series | DDR3-1666 | 
5. | M D |  | Broadwell | 14 nm | 4C+G | 6/2015 |  | 9 Series | DDR3-1866 | 
 |  |  | Skylake | 14 nm | 4C+G | 10/2015 | M: BGA 1356 D: LGA 1151 | Series | DDR4-2133 | 
6. | M D |  |  |  |  |  |  |  |  | 
7. | M D |  | Kaby Lake | 14 nm | 4C + G | 8/2016 |  | 200 Series | DDR4-2400 | 
8. | M D |  | Coffee Lake | 14 nm | 6C +G | 10/2017 | M: BGA 1440 D: LGA 1151 | 300 Series | DDR4-2666 | 
8. | M |  | Amber Lake | 14 nm | 2C+G | 8/2018 | BGA 1515 | 300 Series | LPDDR3-2133 | 
8. | M |  | Whiskey Lake | 14 nm | 4C+G | 8/2018 | BGA 1528 | 300 Series | DDR4-2400 | 
9. | D |  |  |  |  |  |  |  |  | 
 |  |  | Coffee Lake R. | 14 nm | 8C +G | 10/2018 | LGA 1151 | 300 Series | DDR4-2666 | 
 |  |  | Comet Lake | 14 nm | 10C +G | 8/2019 | BGA 1528 LGA 1200 | 400 Series | DDR4-2666 | 
10. | M D |  |  |  |  |  |  |  |  | 
11. | D |  | Rocket Lake | 14 nm | 8C +G | 3/2021 | LGA 1200 | 400 Series | DDR4-3200 | 

## Slide 103: 3.2 How have Intel’s Core 2-based client lines evolved until now? (8)
Raising max. core counts beyond 4 in Core 2-based client processors -2
Gen.C | Seg-ment | Attaching memory | Processor | Techno- logy | Max. core count | Date of intro. | Socket | PCH | Mem. speed (up to) | Mem. channels
8. | M | Attaching memory to the processor die | Cannon Lake | 10 nm | 2C | 5/2018 | BGA | n.a. | DDR4-2400 | 2
10. | M |  | Ice Lake | 10 nm | 4C+G | 7/2019 | Y: BGA 1377 U: BGA 1526 | 300-series | DDR4-3733 | 
11. | M D |  | Tiger Lake | 10 nm | 8C+G | 09/2020 | UP3: BGA 1449 UP4: BGA 1598 B/H: BGA 1787 | 400-series | LPDDR4x-4267 LPDDR5x-5400 | 
12. | M D |  | Alder Lake | 10 nm (Intel 7) | 8C+8C+G | 11/2021 | M: BGA 1744 D: LGA 1700 | 600-series | DDR5-4800 | 4x 32-bit
13 | M D |  | Raptor Lake | 10 nm (Intel 7) | 8C+16C+G | 09/2022 | LGA 1700 | 700-series | DDR5-5600 | 

## Slide 104: 3.2 How have Intel’s Core 2-based client lines evolved until now? (9)
3-wide
2-wide
4-wide
Width of Intel’s and AMD’s basic microarchitectures
5-wide
Intel
Pentium
(1993)
Pentium II (Pentium Pro) 1996)
Pentium III (1999)
Pentium 4 (2000)
AMD
Core 2 (2006)
until
Broadwell (2014)
Skylake (2015)
and subsequent
symmetrical multicores
K7 Athlon (1998)
K8 (Hammer)-based
designs (2003)
K10 (Barcelona/Phenom) based lines (2007)
K10.5 (Shanghai etc.)
based lines (2008)
K15 Bulldozer-based
lines (2011)
Zen-based lines (2017)
K5 (1996)
K6 (1997)
Figure: Evolution of the CPU core widths in Intel’s and AMD’s basic microarchitectures
6-wide
Alder Lake
(2021)
(big.LITTLE
configuration)
Wider CPU cores result in higher performance, so both firms widened their cores (see below).
3.2.3 How have Intel and AMD widened the core widths of their processors?
We point out that one of the reasons why Intel’s Core 2 overtook the performance
leadership from AMD’s K8 was its increased core width (4 vs. 3).
Subsequently, Intel laid further great emphasis on widening their CPU cores.
The main steps of this move were the 5-wide 6. gen. Skylake (2015) and the
6-wide 12th gen. big.little Alder Lake (2021) processor lines.

## Slide 105: 3.2 How have Intel’s Core 2-based client lines evolved until now? (10)
3.2.4 How has the way of attaching memory changed? -1
There are two alternative ways of how memory may be attached to platforms,
as depicted below.
Options for attaching memory to platforms
Attaching memory
to the NB
(MC is integrated
into the NB)
Attaching memory
to the processor
(MC is integrated
onto the processor die)
NB
SB
FSB
Processor
NB
SB
FSB
Processor r
Memory
Memory
MC
MC
NB: North Bridge
SB: South Bridge
MC: Memory Controller NB: North Bridge SB: South Bridge
Up to the Penryn (2008)
From the Nehalem on (2009)

## Slide 106: 3.2 How have Intel’s Core 2-based client lines evolved until now? (11)
How has the way of attaching memory changed? -2
As indicated in the previous Figure, there are two alternatives to how memory may be
connected to platforms:
Attaching memory to the north bridge (NB).
In this case, the MC is implemented in the NB, and data are forwarded to and from
the processor via the FSB.
b) Attaching memory directly to the processor.
In this case, the MC is implemented on the processor die, and data are available
immediately to the processor.
FSB: Front Side Bus
Due to its benefits, Intel switched to directly attaching memory to the processors
along with their server-oriented Nehalem family in 2008 (and in their client-
oriented 2. gen. Nehalem line in 2009), as the following two Tables indicate.
.
Note that attaching memory immediately to the processor is more advantageous
than the other alternative, as it reduces the length of the access path, i.e., it
shortens memory latency.
Another notable benefit of connecting memory directly to the processors becomes
obvious for multiprocessor servers.
In this case, namely, the memory bandwidth of NB-connected memory is limited
by the transfer rate of the FSB, as the FSB has to service all processors, whereas
this limitation does not exist if memory is immediately connected to the
processors by multiple memory channels.

## Slide 107
3.2 How have Intel’s Core 2-based client lines evolved until now? (12)
The way of attaching memory to Intel’s Core 2-based client platforms -1
Gen. | Seg-ment | Attaching memory | Processor | Techno- logy | Max core count | Date of intro. | Socket | MCH/PCH | Mem. speed (up to) | Mem. channels
1. | M D | Attaching memory to the NB | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
 | D |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series | DDR3-1067 | 
 | D |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series | DDR3-1067 | 
 | D | Attaching memory to the processor die | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series | DDR3-1333 | 
 | M D |  | Westmere (M: Arrandale) D: Clarkdale/ | 32 nm | 2C+G | 1/2010 | M:BGA 1288 D:LGA 1156 | 5 Series |  | 
2. | M D |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | M: PGA 988 D: LGA 1155 | 6 series | DDR3-1333 | 
3. | M D |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 |  | 7 series | DDR3-1600 | 
4. | M D |  | Haswell | 22 nm | 4C+G | 6/2013 | M: BGA 1168 D: LGA 1150 | 8 Series | DDR3-1600 | 
4. | D |  | Haswell Refr. | 22 nm | 4C+G | 5/2014 |  | 9 Series | DDR3-1666 | 
5. | M D |  | Broadwell | 14 nm | 4C+G | 6/2015 |  | 9 Series | DDR3-1866 | 
 |  |  | Skylake | 14 nm | 4C+G | 10/2015 | M: BGA 1356 D: LGA 1151 | Series | DDR4-2133 | 
6. | M D |  |  |  |  |  |  |  |  | 
7. | M D |  | Kaby Lake | 14 nm | 4C + G | 8/2016 |  | 200 Series | DDR4-2400 | 
8. | M D |  | Coffee Lake | 14 nm | 6C +G | 10/2017 | M: BGA 1440 D: LGA 1151 | 300 Series | DDR4-2666 | 
8. | M |  | Amber Lake | 14 nm | 2C+G | 8/2018 | BGA 1515 | 300 Series | LPDDR3-2133 | 
8. | M |  | Whiskey Lake | 14 nm | 4C+G | 8/2018 | BGA 1528 | 300 Series | DDR4-2400 | 
9. | D |  |  |  |  |  |  |  |  | 
 |  |  | Coffee Lake R. | 14 nm | 8C +G | 10/2018 | LGA 1151 | 300 Series | DDR4-2666 | 
 |  |  | Comet Lake | 14 nm | 10C +G | 8/2019 | BGA 1528 LGA 1200 | 400 Series | DDR4-2666 | 
10. | M D |  |  |  |  |  |  |  |  | 
11. | D |  | Rocket Lake | 14 nm | 8C +G | 3/2021 | LGA 1200 | 400 Series | DDR4-3200 | 

## Slide 108: 3.2 How have Intel’s Core 2-based client lines evolved until now? (13)
The way of attaching memory to Intel’s Core 2-based client platforms -2
Gen. | Seg-ment | Attaching memory | Processor | Techno- logy | Max. core count | Date of intro. | Socket | PCH | Mem. speed at intro. (up to) | Mem. channels
8. | M | Attaching memory to the processor die | Cannon Lake | 10 nm | 2C | 5/2018 | BGA | n.a. | DDR4-2400 | 2
10. | M |  | Ice Lake | 10 nm | 4C+G | 7/2019 | Y: BGA 1377 U: BGA 1526 | 300-series | LPDDR4-3733 DDR4-3200 | 
11. | M D |  | Tiger Lake | 10 nm | 8C+G | 09/2020 | UP3: BGA 1449 UP4: BGA 1598 B/H: BGA 1787 | 400-series | LPDDR4x-4267 DDR4-3200 | 
12. | M D |  | Alder Lake | 10 nm (Intel 7) | 8C+8C+G | 11/2021 | M: BGA 1744 D: LGA 1700 | 600-series | DDR5-4800 DDR4-3200 | 4x 32-bit
13 | M D |  | Raptor Lake | 10 nm (Intel 7) | 8C+16C+G | 09/2022 | LGA 1700 | 700-series | DDR5-5600 DDR4-3200 | 

## Slide 109: 3.2 How have Intel’s Core 2-based client lines evolved until now? (14)
Contrasting Intel’s move to attach memory to the processor die with related
developments of other firm’s -1
Options for attaching memory to platforms
Attaching memory to the processor die
Attaching memory to the NB
POWER4 (2C) (2001)
POWER5 (2C) (2005)
and subsequent POWER families
Montecito (2C) (2006)
Opteron server lines (2C) (2003)
and all subsequent AMD lines
Core 2 Duo line (2C) (2006)
and all preceding Intel lines
Core 2 Quad line (2x2C) (2006/2007)
Penryn line (2x2C) (2008)
Nehalem lines (4) (2008)
and all subsequent Intel lines
Examples
Tukwila (4C) (2010)
AMD’s K7 lines (1C)
(1999-2003)
UltraSPARC III (2001)
and all subsequent Sun models
UltraSPARC II (1C) (~1997)
HP PA-7100 (1992)
HP PA-7150 (1994)
and subsequent PA models
HP PA-7000 (1991)

## Slide 110: 3.2 How have Intel’s Core 2-based client lines evolved until now? (15)
Contrasting Intel’s move to attach memory to the processor die with related
developments of other firm’s -2
As the previous Figure indicates, Intel was quite late in attaching memory directly to
the processor, for example, AMD did it about 5 years earlier.

## Slide 111: 3.2 How have Intel’s Core 2-based client lines evolved until now? (16)
3.2.5 At which rate have memory speeds raised in Core 2-based client processors?
In the following Figure, we show how supported memory technologies evolved.
While using this data and a logarithmic representation, we get the following graph
for the growth rate of memory speeds.

## Slide 112: 3.2 How have Intel’s Core 2-based client lines evolved until now? (17)

1600
3200
1333
1862
2133
2400
2666
2793
Year
2010
09
11
12
13
14
16
2015
17
18
2020
19
*
*
*
*
*
*
*
*
*
SB
IB
HW
SKL4
KBL
CFL
ICL
TGL
4266
08
1066
PN
*
*
NH1
NH2
DDR5
DDR3 ~ 2x /8 years
3458
MT/s
BW
3733
*
*
5200
4800
21
22
ALL
RTL
*
*
*
*
LPDDR4x
LPDDR4,
DDR4 ~ 2x /8 years
5600
At which rate have memory speeds raised in Core 2-based client processors? -2

## Slide 113: 3.2 How have Intel’s Core 2-based client lines evolved until now? (18)
At which rate have memory speeds raised in Core 2-based client processors? -3
The resulting graph shows the exponential growth of memory rates of memories
manufactured by the same technology, while their memory rates doubled roughly
in 8 years.
32-bit LPDDR4/4x and DDR5 memories evolved approximately by the same path
as 64-bit DDR3 memories did, whereas DDR4 memories have roughly the same
growth rate but achieve about 15 % less transfer rates.
Also, we point out that Intel’s 10 nm processors (from Ice Lake (ICL) to Raptor Lake
(RTL) in the Figure) support both DDR4 and DDR5 memories, whereas all families
mentioned above, support the same DDR4 transfer rate of DDR4-3200.
LPDDR: Low Power DDR

## Slide 114: 3.2 How have Intel’s Core 2-based client lines evolved until now? (19)
3.2.6 How many memory channels client processors provide to serve
CPU cores? -1
First let’s review related data concerning client processors.

## Slide 115
3.2 How have Intel’s Core 2-based client lines evolved until now? (20)
Gen. | Seg-ment | Attaching memory | Processor | Techno- logy | Max core count | Date of intro. | Socket | MCH/PCH | Mem. speed (up to) | Mem. channels
1. | M D | Attaching memory to the NB | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
 | D |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series | DDR3-1067 | 
 | D |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series | DDR3-1067 | 
 | D | Attaching memory to the processor die | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series | DDR3-1333 | 
 | M D |  | Westmere (M: Arrandale) D: Clarkdale/ | 32 nm | 2C+G | 1/2010 | M:BGA 1288 D:LGA 1156 | 5 Series |  | 
2. | M D |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | M: PGA 988 D: LGA 1155 | 6 series | DDR3-1333 | 
3. | M D |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 |  | 7 series | DDR3-1600 | 
4. | M D |  | Haswell | 22 nm | 4C+G | 6/2013 | M: BGA 1168 D: LGA 1150 | 8 Series | DDR3-1600 | 
4. | D |  | Haswell Refr. | 22 nm | 4C+G | 5/2014 |  | 9 Series | DDR3-1666 | 
5. | M D |  | Broadwell | 14 nm | 4C+G | 6/2015 |  | 9 Series | DDR3-1866 | 
 |  |  | Skylake | 14 nm | 4C+G | 10/2015 | M: BGA 1356 D: LGA 1151 | Series | DDR4-2133 | 
6. | M D |  |  |  |  |  |  |  |  | 
7. | M D |  | Kaby Lake | 14 nm | 4C + G | 8/2016 |  | 200 Series | DDR4-2400 | 
8. | M D |  | Coffee Lake | 14 nm | 6C +G | 10/2017 | M: BGA 1440 D: LGA 1151 | 300 Series | DDR4-2666 | 
8. | M |  | Amber Lake | 14 nm | 2C+G | 8/2018 | BGA 1515 | 300 Series | LPDDR3-2133 | 
8. | M |  | Whiskey Lake | 14 nm | 4C+G | 8/2018 | BGA 1528 | 300 Series | DDR4-2400 | 
9. | D |  |  |  |  |  |  |  |  | 
 |  |  | Coffee Lake R. | 14 nm | 8C +G | 10/2018 | LGA 1151 | 300 Series | DDR4-2666 | 
 |  |  | Comet Lake | 14 nm | 10C +G | 8/2019 | BGA 1528 LGA 1200 | 400 Series | DDR4-2666 | 
10. | M D |  |  |  |  |  |  |  |  | 
11. | D |  | Rocket Lake | 14 nm | 8C +G | 3/2021 | LGA 1200 | 400 Series | DDR4-3200 | 
*
Number of memory channels provided in Core 2-based client processors -1

## Slide 116: 3.2 How have Intel’s Core 2-based client lines evolved until now? (21)
Gen. | Seg-ment | Attaching memory | Processor | Techno- logy | Max. core count | Date of intro. | Socket | PCH | Mem. speed (up to) | Mem. channels
8. | M | Attaching memory to the processor die | Cannon Lake | 10 nm | 2C | 5/2018 | BGA | n.a. | DDR4-2400 | 2
10. | M |  | Ice Lake | 10 nm | 4C+G | 7/2019 | Y: BGA 1377 U: BGA 1526 | 300-series | DDR4-3733 LPDDR4-3733 | 4x32-bit
11. | M D |  | Tiger Lake | 10 nm | 8C+G | 09/2020 | UP3: BGA 1449 UP4: BGA 1598 B/H: BGA 1787 | 400-series | LPDDR4x-4267 LPDDR5x-5400 | 
12. | M D |  | Alder Lake | 10 nm (Intel 7) | 8C+8C+G | 11/2021 | M: BGA 1744 D: LGA 1700 | 600-series | DDR5-4800 DDR4-3200 | 4x 32-bit
13 | M D |  | Raptor Lake | 10 nm (Intel 7) | 8C+16C+G | 09/2022 | LGA 1700 | 700-series | DDR5-5600 DDR4-3200 | 
Number of memory channels provided in Core 2-based client processors -2
2
Note that DDR5 memory (as well as LPDDR4/LPDDR5/LPDDR4x memories) have 32-bit
wide memory channels rather than 64-bit channels, as previous DDR-DDR4 memories.
Clearly, four 32-bit wide memory channels equal two 64-bit channels.

## Slide 117: 3.2 How have Intel’s Core 2-based client lines evolved until now? (22)
As data in the above Tables indicates, Intel implemented only two 64-bit memory channels
in their client processors until now, whereas core counts have increased from 2 to 24.
How many memory channels client processors provide to serve CPU cores? -2

## Slide 118: 3.2 How have Intel’s Core 2-based client lines evolved until now? (23)
How can only two 64-bit memory channels remain sufficient for Core 2-based
client processors while core counts have raised dynamically from 2 to 24?
Obviously, while core counts rise, the per-core memory bandwidth should also be preserved
to avoid a memory bottleneck when supplying instructions and data.
In the following Table, we provide data for checking this critical figure for Intel’s
high core count client processors.

## Slide 119: 3.2 How have Intel’s Core 2-based client lines evolved until now? (24)
Generation | Introduced | Processor line | Max. core count | Max. Memory rate | Per-core memory bandwidth GB/s
1. | 06/2006 | Core 2 | 2 | DDR2-800 | 6.4
 | 06/2009 | Nehalem | 4 | DDR3-1333 | 5.4
8. | 10/2017 | Coffee Lake | 6 | DDR4-2666 | 7.2
9. | 10/20118 | Coffee Lake R. | 8 | DDR4-2666 | 5.4
10. | 08/2019 | Comet Lake | 10 | DDR4-2666 | 4.2
12. | 11/2021 | Alder Lake | 8+8 | DDR5-4800 | 4.8
13. | 10/2022 | Raptor Lake | 8+16 | DDR5-5600 | 3.7
Table: Per-core memory bandwidth of client processors with increased core counts
Per core memory bandwidth of Core 2-based client processors with increased
core counts
Above data reveals that per-core memory bandwidth could more or less be sustained
in Intel’s Core 2-based client processors while core counts have raised from 2 to 24.
This has been enabled by a suitable intense rise in memory speeds achieved
by the striking evolution of memory technology from DDR2 to DDR5.

## Slide 120
3.3 How was integrated graphics introduced and
has evolved in Intel’s Core 2 line?
3.3.1 Integrated graphics of the Core 2 line –
its introduction and overview
3.3.3 Case example: The 12th gen. Xe LP GPU included
in 11th gen. Tiger Lake processors
3.3.2 Evolution of key features of Intel’s graphics families
Only the graphics slides 1, 2, 7, 8 (of Section 3.3.1) and
slides 6-10 (of Section 3.3.2) are discussed in the Lecture.
Notes: 120

## Slide 121
3.3.1 Integrated graphics of the Core 2 line –
its introduction and overview
Notes: 121

## Slide 122: 3.3.1 Integrated graphics of the Core 2 line – its introduction and overview (1)
Vertex
Edge
Surface
3.3.1 Integrated graphics of the Core 2 line – its introduction and overview
Vertices in graphics
have three spatial coordinates (FP32 data), and
supplementary information necessary to render the object, such as
color (RGB)
texture
reflectance properties
etc.
Triangle representation of objects in graphics processing
Basics of processor graphics

## Slide 123: 3.3.1 Integrated graphics of the Core 2 line – its introduction and overview (2)
Triangle mesh representation of objects in graphics processing
Example: Triangle mesh representation of a dolphin [103]
Graphics software and hardware operate more efficiently on a group of triangles,
called triangle meshes rather than on individual triangles, so graphics objects
are typically represented by triangle meshes.
Note that all vertices
are given as SP FP data.

## Slide 124: 3.3.1 Integrated graphics of the Core 2 line – its introduction and overview (3)
Shaders (in graphics)
Dedicated HW units
for vertex, pixel ,
geometry shaders)
(Beginning with the
shader model 4.0)
(2006)
Figure:
Various
shader
designs
[107]
Recently, the designation shader refers to graphics routines that run on the GPU’s
shader core and perform graphics tasks e.g., on vertices or pixels of 2D/3D objects.
Such a kind of graphics layout is called unified shader design.
By contrast, early shaders (from the beginning of the 2000s) were yet implemented
by specific hardware (called discrete shader design), as indicated in the following Figure.

## Slide 125: 3.3.1 Integrated graphics of the Core 2 line – its introduction and overview (4)
Main types of shaders in GPUs
Shaders
Geometry shaders
Vertex shaders
Pixel shaders
(Fragment shaders)
Transform each vertex’s
3D-position in the virtual space
to the 2D coordinate,
at which it appears on the screen
Calculate the color
of the pixels
Can add or remove
vertices from a mesh
of vertices
Shader: graphics processing algorithm

## Slide 126: 3.3.1 Integrated graphics of the Core 2 line – its introduction and overview (5)
Graphics APIs (like Microsoft’s DirectX or OpenGL assume the triangle representation
of graphics objects.
Further on, the efficient use of shaders in graphics APIs requires a certain
standardization in form of shader models.
Shader models
Shader models lay down the programming environment of shaders,
including presumed data types, register set etc.
During the evolution of graphics processing vertex and pixel shader models
became unified, as discussed next.

## Slide 127: 3.3.1 Integrated graphics of the Core 2 line – its introduction and overview (6)
unified instruction set,
unified programming resources (e.g. temporary and constant registers).
Convergence of the vertex and pixel shader models
Early shader models (models 2 and 3) had different precision requirements,
implying different data types, register sets and instruction sets (i.e. ISAs).
These models became integrated in the shader model 4, that was introduced
with DirectX10 in 2006 [105].
The unified Shader model 4 declares
Unified precision requirements (FP32) for both vertex and pixel shaders,
the possibility to use new data formats,
Note that due to the unified precision requirement of vertex and pixel shaders
graphics computation needs a vast number of FP32 execution resources.

## Slide 128: 3.3.1 Integrated graphics of the Core 2 line – its introduction and overview (7)
How has integrated graphics evolved in Core 2-based client processors?
Implementation of integrated graphics
In the North Bridge
integrated GPU
On-die
integrated GPU
Intel’s Pentium III to Core 2 Nehalem
processors (1999 – 2009),
first in Intel’s 810 NB (1999)
then in subsequent implementations
P
South Bridge
Mem.
NB
GPU
South Bridge
Mem.
NB
P
GPU
CPU
Periph. Contr.
Mem.
CPU
GPU
P
Intel’s Core 2 Westmere-based
DT and mobile processors
(1/2010)
M: Mobile LT: Laptop D: Desktop NB: North Bridge
CPU and GPU on separate dies
in a multi-chip package (MCP)
On-package
integrated GPU (MCP)
Intel’s Atom-based Pineview (LT, 1/2011)
and subsequent processors
Intel’s Sandy Bridge (DT, 1/2011) and
subsequent processors
Integrated graphics emerged in three steps: first, GPUs became integrated into the NB,
then, GPUs and CPUs were implemented on separate dies, which were encased in the same package,
finally, GPUs were integrated into the CPU die, as shown below.

## Slide 129: 3.3.1 Integrated graphics of the Core 2 line – its introduction and overview (8)
Intel’s HD and Xe graphics families
HD graphics
(From the Westmere family on
(implementing on-package integrated graphics) (2010)
up to the 10th gen. 14 nm
Comet Lake family (2019)
Xe graphics
(From the 10th gen 10 nm
Ice Lake family on (2019)
How have Intel’s graphics families evolved?
Figure: Intel’s HD and Xe graphics families
Note that Intel designates both their Comet Lake and Ice Lake lines as 10th generation.
Intel has two advanced graphics families; the HD graphics and the Xe graphics,
as shown below.
The HD graphics was introduced along with the Core 2 Westmere family (2010), but
it was yet implemented as on-package integrated graphics.
Next, Intel integrated HD graphics on-die in the Sandy Bridge line (2011) and used
HD graphics in all subsequent families up to all 14 nm processors (up to 2019).
The subsequent, more advanced Xe graphics is a complete re-design targeting
all major market segments, from client processors, used for gaming to
data centers with HPC workloads.
The Xe graphics appeared along with 10 nm client processors, first in Intel’s
10th generation Ice Lake line in 2019, as indicated in the following Table.

## Slide 130
Intel Core generation | Arch. gen. | Graphics gen. | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version at intro.
Westmere | -- | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 2nd | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 3rd | 7th | HD 2500 | GT1 | 1 (2x3? EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 4th | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 5th | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 6th | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Overview and key features of Intel’s HD graphics family -1 (based on [20])
3.3.1 Integrated graphics of the Core 2 line – its introduction and overview (9)

## Slide 131
Overview and key features of Intel’s HD graphics family -2 (based on [20])
3.3.1 Integrated graphics of the Core 2 line – its introduction and overview (10)
Intel Core generation | Arch. gen. | Graphics gen. | Models | Graphics Technology level | No. of HD graphics slices/Xe subslices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version at intro.
Kaby Lake | 7th | 9th | HD 610 | GT1 | 1 | 12 | -- | 4.5 | 12 | 2.1?
 |  |  | HD 615 | GT2 | 1 | 24 |  |  |  | 
 |  |  | HD 620 |  |  |  |  |  |  | 
 |  |  | HD 630 |  |  |  |  |  |  | 
 |  |  | HD 640 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  |  | HD 650 |  |  |  | 64 MB |  |  | 
Kaby Lake Refr. to Comet Lake | 8th - 10th | 9th | UHD 610 | GT1 | 1 | 12 | n.a. |  |  | 
 |  |  | UHD 615 | GT2 | 1 | 24 |  |  |  | 
 |  |  | UHD 617 |  |  |  |  |  |  | 
 |  |  | UHD 620 |  |  |  |  |  |  | 
 |  |  | UHD 630 |  |  |  |  |  |  | 
 |  |  | UHD 645 | GT3 | 2 | 48 |  |  |  | 
 |  |  | UHD 655 |  |  |  |  |  |  | 

## Slide 132
Overview and key features of Intel’s Xe graphics family (based on [20])
3.3.1 Integrated graphics of the Core 2 line – its introduction and overview (11)
Intel Core generation | Arch. gen. | Graphics gen. | Models | Graphics Technology level | No. of HD graphics slices/Xe subslices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version at intro.
Ice Lake | 10th | 11th | Iris Xe | G1 | 4 | 32 | n.a. | 4.6? | 12.1 | 2.1
 |  |  | Iris Xe | G4 | 6 | 48 |  |  |  | 
 |  |  | Iris Xe | G7 | 8 | 64 |  |  |  | 
Tiger Lake | 11th | 12th | Iris Xe LP | G1 | 2 | 32 | n.a. |  |  | 3.0
 |  |  | Iris Xe LP | G4 | 3 | 48 |  |  |  | 
 |  |  | Iris Xe LP | G7 | 5 | 80 |  |  |  | 
 |  |  | Iris Xe LP | G7 | 6 | 96 |  |  |  | 
Alder Lake-S | 12th | 12th | Iris Xe UHD 770 | na. | na. | 80/96 32/64 | n.a. |  |  | 
Remark
AMD’s chief graphics designer, Raja Koduri, left the firm and joined Intel in 2017
to become the lead graphics architect.
The Xe graphics family was designed under his leadership.

## Slide 133
3.3.2 How have key features of Intel’s graphics families evolve?
Notes: 133

## Slide 134: 3.3.2 How have key features of Intel’s graphics families evolve? (1)
3.3.2 How have key features of Intel’s graphics families evolve?
Subsequently, we discuss only three features out of those presented in the previous
overview Tables due to volume restrictions of our Lecture, as follows:
a) the designation of Intel’s graphics generation,
b) the number of graphics execution units and
c) API support
API: Application Program Interface

## Slide 135: 3.3.2 How have key features of Intel’s graphics families evolve? (2)
Up to and including the 11th gen. Tiger Lake line (2020), Intel named their graphics and
microarchitecture generations differently, as the next Table shows.
a) How Intel designates their graphics generations? -1

## Slide 136
Intel Core generation | Arch. gen. | Graphics gen. | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version at intro.
Westmere | -- | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 2nd | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 3rd | 7th | HD 2500 | GT1 | 1 (2x3? EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 4th | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 5th | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 6th | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Designation of Intel’s graphics generations -1 (based on [20])
3.3.2 How have key features of Intel’s graphics families evolve? (3)

## Slide 137: 3.3.2 How have key features of Intel’s graphics families evolve? (4)
How Intel designates their graphics generations? -2
In the previous Table, e.g., the Sandy Bridge line is called the 2nd gen. Core 2 family,
but it has the 6th gen. graphics.
The reason for this inconsistency lies in the history of Intel’s graphics development,
as Intel designated their previous graphics implementations as the 1st to 5th
generation graphics.
Intel’s first GPUs appeared in 1998, called first-generation graphics.
They were discrete GPUs (mounted on GPU cards or directly onto the mainboard).
Shortly after that, in 1999, Intel integrated their GPUs into the NB part of
the chipset (called then the GMCH (Graphics and Memory Controller)).
In 2002, Intel enhanced its graphics design and called it the 2nd generation.
3rd and 4th gen. chipset integrated graphics followed along with Pentium 4 and
first Core 2 processors (up to the Nehalem family).
In the next step of graphics evolution, Intel integrated the graphics and CPU dies
into the same package and called it the 5th generation graphics, used with
the Westmere line.
Historical remarks

## Slide 138: 3.3.2 How have key features of Intel’s graphics families evolve? (5)
How Intel designates their graphics generations? -3
Note that lately, Intel adjusted the naming of their graphics and microarchitecture
generations in their 12th gen. Alder Lake line (in 2021), as shown below.
Intel Core generation | Arch. gen. | Graphics gen. | Models | Graphics Technology level | No. of HD graphics slices/Xe subslices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version at intro.
Ice Lake | 10th | 11th | Iris Xe | G1 | 4 | 32 | n.a. | 4.6? | 12.1 | 2.1
 |  |  | Iris Xe | G4 | 6 | 48 |  |  |  | 
 |  |  | Iris Xe | G7 | 8 | 64 |  |  |  | 
Tiger Lake | 11th | 12th | Iris Xe LP | G1 | 2 | 32 | n.a. |  |  | 3.0
 |  |  | Iris Xe LP | G4 | 3 | 48 |  |  |  | 
 |  |  | Iris Xe LP | G7 | 5 | 80 |  |  |  | 
 |  |  | Iris Xe LP | G7 | 6 | 96 |  |  |  | 
Alder Lake-S | 12th | 12th | Iris Xe UHD 770 | na. | na. | 80/96 32/64 | n.a. |  |  | 

## Slide 139: 3.3.2 How have key features of Intel’s graphics families evolve? (6)
b) At which rate has Intel raised the number of EUs in their GPUs? -1
EU: Execution Unit
Graphics EUs are the workhorses for graphics computing, capable of performing
beyond a vast number of FP32 operations, 32-bit FX, 64-bit FP, and other
calculations as well, as discussed in an example later.
As graphics performance scales more or less linearly with the number of EUs
available in a GPU, it is worth looking for their number in the overview Tables.
While choosing a logarithmic representation, we get the following graph:

## Slide 140: 3.3.2 How have key features of Intel’s graphics families evolve? (7)
Max. number of graphics EUs available in GPUs of Core 2 processors -1
No of EUs
(log scale)
2006
2008
2010
2012
2014
2016
Year
2018
2020
2022
*
*
*
*
*
*
12
16
40
48
72
96
Sandy
Bridge
Ivy
Bridge
Haswell
Broadwell
Ice Lake
Tiger Lake
≈ 10x in 10 years

## Slide 141: 3.3.2 How have key features of Intel’s graphics families evolve? (8)
At which rate has Intel raised the number of EUs in their GPUs? -2
It is worthwhile to contrast this evidence with Intel’s disclosure of how far graphics
performance within their Core 2 family has been raised (see the next Figure).
The above graph indicates that Intel raised the max. number of graphics EUs
in their GPUs 10-fold in roughly 10 years.

## Slide 142: 3.3.2 How have key features of Intel’s graphics families evolve? (9)
Graphics performance increase in subsequent Core generations, as revealed
by Intel [24] -1
Skylake (2018)
Broadwell (2015)
Haswell (2013)
Ivy Bridge (2012)
Sandy Bridge (2011)

## Slide 143: 3.3.2 How have key features of Intel’s graphics families evolve? (10)
Graphics performance increase in subsequent Core generations, as revealed
by Intel [24] -2
In the preceding Figure, Intel reports a more than 100-fold improvement in
graphics performance achieved with its 6th generation (Skylake) processors.
Nevertheless, this statement must be taken cautiously since Intel compared
their graphics with moderate performance, first or second-gen. graphics,
which were implemented yet as discrete graphics or graphics integrated
into the NB in about 1998/1999 (not specified).
If instead we compare only the graphics performance figures of integrated
graphics implementations (i.e., performance figures of the 2nd gen. and 6th gen.
Core 2 processors) we get a more realistic improvement of about 140/25=5,6.
This value is pretty much the same as the ratio of the EUs in the 6th and
2nd generation Core 2 processors: 72/12=6.
It follows that graphics performance is roughly proportional to the number of
graphics EUs, as expected, since graphics EUs provide the computing resources
for the needed graphics computations.

## Slide 144: 3.3.2 How have key features of Intel’s graphics families evolve? (11)
How the performance of Intel’s recent graphics compares to competing
implementations in 2022 [24]
Above example indicates that Intel’s recent 13th gen. graphics provides less performance
than AMD’s graphics. [62]

## Slide 145: 3.3.2 How have key features of Intel’s graphics families evolve? (12)
c) How far Intel’s graphics supports graphics APIs and the OpenCL language?
Subsequent graphics generations provide support for more and more advanced
graphics APIs (OpenGL, DirectX) and for the OpenCL language, as the next Tables
indicate.
OpenGL (Open Graphics Library) is a cross-language, cross-platform API for
rendering 2D or 3D graphics.
It was developed by Silicon Graphics, managed since 2006 by the Khronos Group.
In 2018, Apple deprecated its use on all their platforms (iOS, macOS, and tvOS),
urging developers to switch to their proprietary Metal API.
DirectX is Microsoft’s API; it covers mainly graphics, audio, and networking and is used
on Microsoft and Xbox platforms primarily.
OpenCL (Open Computing Language) is an open, royalty-free standard for
cross-platform, parallel programming for data-intensive applications on a GPU,
owned by the Chronos Group.
Remark

## Slide 146: 3.3.2 How have key features of Intel’s graphics families evolve? (13)
Intel Core generation | Arch. gen. | Graphics gen. | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Westmere | -- | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 2nd | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 3rd | 7th | HD 2500 | GT1 | 1 (2x3? EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 4th | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 5th | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 6th | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Support of graphics APIs and OpenCL in Intel’s graphics -1

## Slide 147: 3.3.2 How have key features of Intel’s graphics families evolve? (14)
Intel Core generation | Arch. gen. | Graphics gen. | Models | Graphics Technology level | No. of graphics slices/Xe subslices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Kaby Lake | 7th | 9th | HD 610 | GT1 | 1 | 12 | -- | 4.5 | 12 | 2.1?
 |  |  | HD 615 | GT2 | 1 | 24 |  |  |  | 
 |  |  | HD 620 |  |  |  |  |  |  | 
 |  |  | HD 630 |  |  |  |  |  |  | 
 |  |  | HD 640 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  |  | HD 650 |  |  |  | 64 MB |  |  | 
Kaby Lake Refr. to Comet Lake | 8th - 10th | 9th | UHD 610 | GT1 | 1 | 12 | n.a. |  |  | 
 |  |  | UHD 615 | GT2 | 1 | 24 |  |  |  | 
 |  |  | UHD 617 |  |  |  |  |  |  | 
 |  |  | UHD 620 |  |  |  |  |  |  | 
 |  |  | UHD 630 |  |  |  |  |  |  | 
 |  |  | UHD 645 | GT3 | 2 | 48 |  |  |  | 
 |  |  | UHD 655 |  |  |  |  |  |  | 
Ice Lake | 10th | 11th | Iris Xe | G1 | 4 | 32 | n.a. | 4.6 | 12.1 | 2.1
 |  |  | Iris Xe | G4 | 6 | 48 |  |  |  | 
 |  |  | Iris Xe | G7 | 8 | 64 |  |  |  | 
Tiger Lake | 11th | 12th | Iris Xe LP | G1 | 2 | 32 | n.a. |  |  | 3.0
 |  |  | Iris Xe LP | G4 | 3 | 48 |  |  |  | 
 |  |  | Iris Xe LP | G7 | 5 | 80 |  |  |  | 
 |  |  | Iris Xe LP | G7 | 6 | 96 |  |  |  | 
Alder Lake | 12th | 12th | Iris Xe UHD 770 | na. | na. | 32/64 80/96 | n.a. |  |  | 
Support of graphics APIs and OpenCL in Intel’s graphics -2

## Slide 148
3.3.3 Case example: The 12th gen. Xe LP GPU
included in 11th gen. Tiger Lake processors
Notes: 148

## Slide 149: 3.3.3 Case example: The 12th gen. Xe LP GPU of 11th gen. Tiger Lake processors (1)
Intel’s 12th gen. Xe LP GPUs are built up of modules where each module includes dual
subslices with shared thread control [23].
The Figure shows a G7 level implementation, where there are three modules with 6 subslices.
3.3.3 Case example: The 12th gen. Xe LP GPU of 11th gen. Tiger Lake processors

## Slide 150: 3.3.2 Case example: The 12th gen. Xe LP GPU of 11th gen. Tiger Lake processors (2)
Graphics subslices of 12th gen. Xe LP GPUs of 11th gen. Tiger Lake processors [22]
Figure: Graphics subslice of Intel’s
12th gen. Xe LP GPUs [22]
Subslices are subunits of slices, including
among others, 16 EUs (Execution Units)
for performing FX/FP computations.
There are various numbers of subslices
in Intel’s different processor models,
e.g., 2 - 6 in 12th gen. Xe LP GPUs, as seen
before.
Consequently, 12th gen. Xe LP GPUs may
include up to 6x16=96 EUs.
Each two EUs operates in tandem by sharing
thread control and branch processing,
as indicated in the next Figure.

## Slide 151: 3.3.2 Case example: The 12th gen. Xe LP GPU of 11th gen. Tiger Lake processors (3)
Layout of 12th gen. graphics EUs (actually 2 EUs) of Tiger Lake processors [22]
On the IP 0 there are two 8-wide (8x32-bit)
SIMD ALUs (an FP and an FX ALU) available,
they operate exclusively and can perform up to
whereas on the IP 1 there is an
Extended Math (EM) unit available,
that can perform up to two
Extended Math (EM) operations
(to calculate trigonometric functions etc.)
8 FP32, 16 FP16 FMA operations or
8 FX32, 16 FX16, 32 FX8 FMA operations,

## Slide 152: 3.3.2 Case example: The 12th gen. Xe LP GPU of 11th gen. Tiger Lake processors (4)
Data in the above Table takes into account that EUs may perform FMA
(Fused Multiply-Add) operations.
Summing up the computing capabilities of 12th gen. graphics EUs [23]
Computing capabilities of 12th gen. EUs (operations/clock/EU) | 
 | Xe LP (Gen 12)
FP32 | 16
FP16 | 32
FX32 | 16
FX16 | 32
FX8 (INT8) | 64

## Slide 153: 3.3.2 Case example: The 12th gen. Xe LP GPU of 11th gen. Tiger Lake processors (5)
Example floor plan of a 12th gen. Alder Lake processor die with Xe LP graphics
including 2x16 graphics EUs [31] -1
TMU: Texture Mapping Unit of the GPU

## Slide 154: 3.3.2 Case example: The 12th gen. Xe LP GPU of 11th gen. Tiger Lake processors (4)
Example floor plan of a 12th gen. Alder Lake processor die with Xe LP graphics
including 2x16 graphics EUs [31] -2
This picture shows major units of the processor, such as the 8 big cores (called.
Golden Cove), the 8 little cores (designated as Gracemont), the Ring bus
interconnecting the big cores with all significant parts, the IDI link (In-Die interface)
linking the little cores to a global crossbar, the GPU, Memory Channel Control,
Display Control, Media engine, 1x16 or 2x8 PCIeGen5 lanes etc.

## Slide 155
4. Evolution of HEDT (High-End Desktop) processors
Only slides 1-11 and 30 are discussed in the Lecture.
Notes: 155

## Slide 156: 4. Evolution of HEDT (High-End Desktop) processors (1)
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smarphones
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smartphones
Desktops
Servers
Recent major processor categories of Intel
Xeon E7/E5/E3
Platinum/Gold etc.
Clients
(Desktops/Laptops)
Core i9/i7/i5/i3
(Basic architectures)
HEDTs
(High-End Desktops)
Core i7/i9
(Extreme Edition
or X models)
4. Evolution of HEDT (High-End DeskTop) processors -1
Mobiles
(Tablets, Smartphones)
Atom lines
Atom lines
(+ LP Core models)

## Slide 157: 4. Evolution of HEDT (High-End Desktop) processors (2)
Evolution of HEDT (High-End DeskTop) processors -2
In this Section
first, we discuss what HEDT processors are and how they emerged,
subsequently, we sum up the features they have to provide and discuss their
evolution,
finally, we are concerned with their not-too-rosy outlook.

## Slide 158: 4. Evolution of HEDT (High-End Desktop) processors (3)
What are HEDT (High-End DeskTop) processors?
HEDT processors belong to a market segment between “usual DT” and workstation (W) processors.
On the one hand, they provide more performance than “usual” DT processors but
less than workstation processors.
On the other hand, they aim at individuals, like graphics enthusiasts, hardcore
gamers, and multimedia content creators, rather than enterprises.
HEDTs are typically used for demanding graphics tasks, like 3D rendering, video
editing, or gaming.

## Slide 159: 4. Evolution of HEDT (High-End Desktop) processors (4)
Hardcore gamer scenario [25]

## Slide 160: 4. Evolution of HEDT (High-End Desktop) processors (5)
When HEDT processors emerged and how they evolved?
Intel coined the term by introducing the Pentium 4 Extreme Edition in 2003, as
shown in the following Figure.

## Slide 161: 4. Evolution of HEDT (High-End Desktop) processors (6)
Intel's introduction of Pentium 4-based Extreme Edition DT processors in 2003
180 nm
130 nm
90 nm

## Slide 162: 4. Evolution of HEDT (High-End Desktop) processors (7)
Subsequent evolution of HEDT processors
In their Core 2 family, Intel continued rolling out HEDT processors while identifying them
first as “Extreme” processors and later by the
tags, as indicated in the next Table that provides an overview of Intel’s HEDT processors.
E (Extreme) or the
X (eXtreme)

## Slide 163: 4. Evolution of HEDT (High-End Desktop) processors (8)
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachm. | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Core 2 Extreme X6800 | 65 nm | 7/2006 | 2C | Via MCH | DDR3-1066 | 32 PCIe 2.0 on the X38 | 2 | X38 | 65 W | LGA 775
Core 2 Extreme QX 6xxx | 65 nm | 11/2006 | 2x2C |  |  |  |  |  | 130 W | LGA 775
 |  |  |  |  |  |  |  |  | 130 W | LGA 775
Core 2 Extreme QX 9650 (Penryn) | 45 nm | 11/2007 | 2x2C |  |  |  |  |  |  | 
Core 2 Extreme QX 9770 (Penryn) | 45 nm | 3/2008 | 2x2C |  | DDR3-1600 | 32 PCIe 2.0 on the X48 | 2 | X48 | 136 W | LGA 775
1. G. Nehalem EE | 45 nm | 11/2008 | 4C | On-die MC | DDR3-1067 | 36 PCIe 2.0 on the X58 | 3 | X58 (Tylersburg) | 130 W | LGA 1366
Westmere EE | 32 nm | 3/2010 | 6C |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 130 W | LGA 1366
Sandy Bridge E | 32 nm | 11/2011 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 40 PCIe 2.0 on-die | 4 | X79 (Patsburg) | 130 W/ 150 W | LGA 2011
Ivy Bridge E | 22 nm | 9/2013 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1866 | 40 PCIe 3.0 on-die | 4 |  | 130 W | LGA 2011
Haswell E | 14 nm | 8/2014 | 8C |  | DDR4-2133 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Broadwell E | 14 nm | 5/2016 | 10C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2400 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Skylake X | 14 nm | 6/2017 | 18C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 140 W | LGA 2066
(Kaby Lake X) | 14 nm | 6/2017 | 4C |  | DDR4-2666 | 16 PCIe 3.0 on-die | 4 | X299 (Basin Falls) | 112 W | LGA 2066
Overview of Intel’s HEDT processors -1

## Slide 164: 4. Evolution of HEDT (High-End Desktop) processors (9)
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachment | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Skylake-X Refresh | 14 nm | 11/2018 | 18C | On-die MC | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 165 W | LGA- 2066
Cascade Lake-X (Server arch.) | 14 nm | 11/2019 | 18C |  | DDR4-2933 | 48 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 165 W | LGA 066
Overview of Intel’s HEDT processors -2

## Slide 165: 4. Evolution of HEDT (High-End Desktop) processors (10)
Remark on AMD’s HEDT processors
Along with their Zen family, AMD also introduced HEDT processors in 2017, calling
them Threadrippers.
With their high core counts (first 16, then 32 and 64) and plenty of PCIe lanes
(first 64, then 128 lanes) AMD provided fierce competition to Intel’s HEDTs and
became dominant in this market segment.
Note
Because of the shaken market situation of HEDTs having occurred in the last few years
we will omit the rest of this Section from our Lecture.

## Slide 166: 4. Evolution of HEDT (High-End Desktop) processors (11)
What are the key features of HEDT processors compared to DT processors?
More PCIe lanes
More cores
More memory channels
Lack of integrated graphics
Unlocked clock multiplier
Higher TDP

## Slide 167: 4. Evolution of HEDT (High-End Desktop) processors (12)
More PCIe lanes
Enthusiast PC gamers or content creators may use up to 3 or 4 discrete
graphics cards, as shown before.
To attach up to 4 graphics cards, with 8 or 16 PCIe lanes required per card,
HEDT processors need at least 4x8=32 PCIe lanes.
This number is considerably more than 16 lanes furnished by DT processors.
Accordingly, initially Intel provided 32 PCIe2.0 lanes for their Core 2-based
HEDT processors and subsequently raised their number up to 48, as shown
in the following Tables.

## Slide 168: 4. Evolution of HEDT (High-End Desktop) processors (13)
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachm. | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Core 2 Extreme X6800 | 65 nm | 7/2006 | 2C | Via MCH | DDR3-1066 | 32 PCIe 2.0 on the X38 | 2 | X38 | 65 W | LGA 775
Core 2 Extreme QX 6xxx | 65 nm | 11/2006 | 2x2C |  |  |  |  |  | 130 W | LGA 775
 |  |  |  |  |  |  |  |  | 130 W | LGA 775
Core 2 Extreme QX 9650 (Penryn) | 45 nm | 11/2007 | 2x2C |  |  |  |  |  |  | 
Core 2 Extreme QX 9770 (Penryn) | 45 nm | 3/2008 | 2x2C |  | DDR3-1600 | 32 PCIe 2.0 on the X48 | 2 | X48 | 136 W | LGA 775
1. G. Nehalem EE | 45 nm | 11/2008 | 4C | On-die MC | DDR3-1067 | 36 PCIe 2.0 on the X58 | 3 | X58 (Tylersburg) | 130 W | LGA 1366
Westmere EE | 32 nm | 3/2010 | 6C |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 130 W | LGA 1366
Sandy Bridge E | 32 nm | 11/2011 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 40 PCIe 2.0 on-die | 4 | X79 (Patsburg) | 130 W/ 150 W | LGA 2011
Ivy Bridge E | 22 nm | 9/2013 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1866 | 40 PCIe 3.0 on-die | 4 |  | 130 W | LGA 2011
Haswell E | 14 nm | 8/2014 | 8C |  | DDR4-2133 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Broadwell E | 14 nm | 5/2016 | 10C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2400 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Skylake X | 14 nm | 6/2017 | 18C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 140 W | LGA 2066
(Kaby Lake X) | 14 nm | 6/2017 | 4C |  | DDR4-2666 | 16 PCIe 3.0 on-die | 4 | X299 (Basin Falls) | 112 W | LGA 2066
Number of PCIe lanes provided in Core 2-based HEDT processors -1

## Slide 169: 4. Evolution of HEDT (High-End Desktop) processors (14)
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachment | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Skylake-X Refresh | 14 nm | 11/2018 | 18C | On-die MC | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 165 W | LGA- 2066
Cascade Lake-X (Server arch.) | 14 nm | 11/2019 | 18C |  | DDR4-2933 | 48 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 165 W | LGA 066
Number of PCIe lanes provided in Core 2-based HEDT processors -2
In addition to this point, in the next Figure we contrast the number of PCIe lanes and
memory channels in Intel’s Core 2-based DT and HEDT processors.

## Slide 170: 4. Evolution of HEDT (High-End Desktop) processors (15)
DT processors: 16 lanes
(1x16 or 2x8 or 1x8+2x4)
PCIe lanes provided on the processor die
HEDT processors: 40+ lanes (typical)
(configurable, e.g. 2x x16 + 1x x8 or 4x x8)
PCIe 3.0 lanes
PCIe 2.0 lanes
PCIe generation
Mem.
P
Periph. Contr.
PCIe
2.0
x16/
2x x8
x16/
2x x8
Mem.
P
Periph. Contr.
PCIe
3.0
Intel 2. gen. Nehalem (Lynnfield) (4C), 2 MCh
with P55 (2009)
Intel Sandy Bridge (4C), 2 MCh with P67 (2011)
P55/P67
Z77/Z87/Z97/
Z170
Intel Ivy Bridge-E (6C), 4 MCh with X79 (2013)
Number of PCIe lanes and memory channels on Core 2-based DT vs. HEDT processors
PCIe
3.0
40-48
configurable
lanes
Mem.
P
Periph. Contr.
X79/Z99/
X299
PCIe
2.0
40
configurable
lanes
Mem.
P
Periph. Contr.
X79
Intel Sandy Bridge-E (6C), 4 MCh with X79 (2011)
Intel Ivy Bridge (4C), 2 MCh with Z77 PCH (2012)
Intel Haswell (4C), 2 MCh with Z87 PCH (2013)
Intel Broadwell (4C), 2 MCh with Z97 PCH (2015)
Intel Skylake-S (4C), 2 MCh with Z170 PCH (2015)
and subsequent lines
40 lanes beginning with
44 lanes beginning with
Intel Skylake-X (18C), 4 MCh with X299 (2017)
48 lanes beginning with
Intel Cascade Lake-X (18C), 4 MCh with X279 (2019)

## Slide 171: 4. Evolution of HEDT (High-End Desktop) processors (16)
b) More cores
Graphics programs operate primarily on pixels, permitting massively parallel execution,
consequently, HEDT processors should have as many cores as feasible by the
available IC technology.
Accordingly, while IC technology evolved, core counts of HEDT processors rose
from 2 to 18 until now (02/2022).

## Slide 172: 4. Evolution of HEDT (High-End Desktop) processors (17)
Core counts on Core 2-based HEDT processors -1
The above HEDT models and lines are unlocked.
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachm. | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Core 2 Extreme X6800 | 65 nm | 7/2006 | 2C | Via MCH | DDR3-1066 | 32 PCIe 2.0 on the X38 | 2 | X38 | 65 W | LGA 775
Core 2 Extreme QX 6xxx | 65 nm | 11/2006 | 2x2C |  |  |  |  |  | 130 W | LGA 775
 |  |  |  |  |  |  |  |  | 130 W | LGA 775
Core 2 Extreme QX 9650 (Penryn) | 45 nm | 11/2007 | 2x2C |  |  |  |  |  |  | 
Core 2 Extreme QX 9770 (Penryn) | 45 nm | 3/2008 | 2x2C |  | DDR3-1600 | 32 PCIe 2.0 on the X48 | 2 | X48 | 136 W | LGA 775
1. G. Nehalem EE | 45 nm | 11/2008 | 4C | On-die MC | DDR3-1067 | 36 PCIe 2.0 on the X58 | 3 | X58 (Tylersburg) | 130 W | LGA 1366
Westmere EE | 32 nm | 3/2010 | 6C |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 130 W | LGA 1366
Sandy Bridge E | 32 nm | 11/2011 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 40 PCIe 2.0 on-die | 4 | X79 (Patsburg) | 130 W/ 150 W | LGA 2011
Ivy Bridge E | 22 nm | 9/2013 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1866 | 40 PCIe 3.0 on-die | 4 |  | 130 W | LGA 2011
Haswell E | 14 nm | 8/2014 | 8C |  | DDR4-2133 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Broadwell E | 14 nm | 5/2016 | 10C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2400 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Skylake X | 14 nm | 6/2017 | 18C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 140 W | LGA 2066
(Kaby Lake X) | 14 nm | 6/2017 | 4C |  | DDR4-2666 | 16 PCIe 3.0 on-die | 4 | X299 (Basin Falls) | 112 W | LGA 2066

## Slide 173: 4. Evolution of HEDT (High-End Desktop) processors (18)
Core counts on Core 2-based HEDT processors-2
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachment | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Skylake-X Refresh | 14 nm | 11/2018 | 18C | On-die MC | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 165 W | LGA- 2066
Cascade Lake-X (Server arch.) | 14 nm | 11/2019 | 18C |  | DDR4-2933 | 48 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 165 W | LGA 066

## Slide 174: 4. Evolution of HEDT (High-End Desktop) processors (19)
Remark
Despite their X tag, the Kaby Lake-X models in fact, do not fit into the traditional
HEDT lines, they are the highest-performance models of the Kaby Lake line and
are intended to be used in the mobile market segment.

## Slide 175: 4. Evolution of HEDT (High-End Desktop) processors (20)
2006
2003
2010
2014
2016
2006
Evolution of core counts in Intel's Core 2-based HEDT lines (Based on [26])
2017
Core 2
Extreme
X6800
Westmere EE
Haswell E
Broadwell E
Core 2
Extreme
QX6700
Skylake X
18
18 CORE
Number of cores
Pentium 4 EE
3.2

## Slide 176: 4. Evolution of HEDT (High-End Desktop) processors (21)
c) More memory channels
To provide enough bandwidth for a higher number of cores than implemented
in DTs, HEDT processors are typically designed with more memory channels than
their DT peers.
In fact, after raising the core count to 6, Intel increased the number of memory
channels first to 3, then to 4, and held on providing 4 channels until now,
as data in the following Tables demonstrate.

## Slide 177: 4. Evolution of HEDT (High-End Desktop) processors (22)
Number of memory channels -1
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachm. | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Core 2 Extreme X6800 | 65 nm | 7/2006 | 2C | Via MCH | DDR3-1066 | 32 PCIe 2.0 on the X38 | 2 | X38 | 65 W | LGA 775
Core 2 Extreme QX 6xxx | 65 nm | 11/2006 | 2x2C |  |  |  |  |  | 130 W | LGA 775
 |  |  |  |  |  |  |  |  | 130 W | LGA 775
Core 2 Extreme QX 9650 (Penryn) | 45 nm | 11/2007 | 2x2C |  |  |  |  |  |  | 
Core 2 Extreme QX 9770 (Penryn) | 45 nm | 3/2008 | 2x2C |  | DDR3-1600 | 32 PCIe 2.0 on the X48 | 2 | X48 | 136 W | LGA 775
1. G. Nehalem EE | 45 nm | 11/2008 | 4C | On-die MC | DDR3-1067 | 36 PCIe 2.0 on the X58 | 3 | X58 (Tylersburg) | 130 W | LGA 1366
Westmere EE | 32 nm | 3/2010 | 6C |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 130 W | LGA 1366
Sandy Bridge E | 32 nm | 11/2011 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 40 PCIe 2.0 on-die | 4 | X79 (Patsburg) | 130 W/ 150 W | LGA 2011
Ivy Bridge E | 22 nm | 9/2013 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1866 | 40 PCIe 3.0 on-die | 4 |  | 130 W | LGA 2011
Haswell E | 14 nm | 8/2014 | 8C |  | DDR4-2133 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Broadwell E | 14 nm | 5/2016 | 10C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2400 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Skylake X | 14 nm | 6/2017 | 18C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 140 W | LGA 2066
(Kaby Lake X) | 14 nm | 6/2017 | 4C |  | DDR4-2666 | 16 PCIe 3.0 on-die | 4 | X299 (Basin Falls) | 112 W | LGA 2066

## Slide 178: 4. Evolution of HEDT (High-End Desktop) processors (23)
Number of memory channels -2
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachment | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Skylake-X Refresh | 14 nm | 11/2018 | 18C | On-die MC | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 165 W | LGA- 2066
Cascade Lake-X (Server arch.) | 14 nm | 11/2019 | 18C |  | DDR4-2933 | 48 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 165 W | LGA 066

## Slide 179: 4. Evolution of HEDT (High-End Desktop) processors (24)
d) Lack of integrated graphics
HEDTs do not provide integrated graphics, as they make use of one or more
high-performance discrete graphics cards; this fact makes the additional
additional use of less-performing integrated graphics superfluous.

## Slide 180: 4. Evolution of HEDT (High-End Desktop) processors (25)
e) Unlocked clock multiplier
Intel’s HEDT processors are typically unlocked, meaning that the clock multiplier
isn’t fixed, i.e., it is variable to allow overclocking.
This feature may be helpful for graphics enthusiasts to raise performance.
(The clock multiplier is a circuit that generates the clock frequency by
multiplying the bus frequency (100/133 MHz) by an integer delivered by
the PCU (Power Control Unit)).

## Slide 181: 4. Evolution of HEDT (High-End Desktop) processors (26)
f) Higher TDP
Clearly, more PCIe lanes, more cores, memory channels, etc. need more power,
so HEDT processors typically have 130 to 165 W power consumption vs. 65 to
95 W, usually consumed by DT processors, as the Tables below indicate.

## Slide 182: 4. Evolution of HEDT (High-End Desktop) processors (27)
TDP (Thermal Design Power) values of Core 2-based HEDT models-1
TDP: Serves as the reference value for designing the cooling system.
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachm. | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Core 2 Extreme X6800 | 65 nm | 7/2006 | 2C | Via MCH | DDR3-1066 | 32 PCIe 2.0 on the X38 | 2 | X38 | 65 W | LGA 775
Core 2 Extreme QX 6xxx | 65 nm | 11/2006 | 2x2C |  |  |  |  |  | 130 W | LGA 775
 |  |  |  |  |  |  |  |  | 130 W | LGA 775
Core 2 Extreme QX 9650 (Penryn) | 45 nm | 11/2007 | 2x2C |  |  |  |  |  |  | 
Core 2 Extreme QX 9770 (Penryn) | 45 nm | 3/2008 | 2x2C |  | DDR3-1600 | 32 PCIe 2.0 on the X48 | 2 | X48 | 136 W | LGA 775
1. G. Nehalem EE | 45 nm | 11/2008 | 4C | On-die MC | DDR3-1067 | 36 PCIe 2.0 on the X58 | 3 | X58 (Tylersburg) | 130 W | LGA 1366
Westmere EE | 32 nm | 3/2010 | 6C |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 130 W | LGA 1366
Sandy Bridge E | 32 nm | 11/2011 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 40 PCIe 2.0 on-die | 4 | X79 (Patsburg) | 130 W/ 150 W | LGA 2011
Ivy Bridge E | 22 nm | 9/2013 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1866 | 40 PCIe 3.0 on-die | 4 |  | 130 W | LGA 2011
Haswell E | 14 nm | 8/2014 | 8C |  | DDR4-2133 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Broadwell E | 14 nm | 5/2016 | 10C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2400 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Skylake X | 14 nm | 6/2017 | 18C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 140 W | LGA 2066
(Kaby Lake X) | 14 nm | 6/2017 | 4C |  | DDR4-2666 | 16 PCIe 3.0 on-die | 4 | X299 (Basin Falls) | 112 W | LGA 2066

## Slide 183: 4. Evolution of HEDT (High-End Desktop) processors (28)
TDP (Thermal Design Power) values of Core 2-based HEDT models -2
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachment | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Skylake-X Refresh | 14 nm | 11/2018 | 18C | On-die MC | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 165 W | LGA- 2066
Cascade Lake-X (Server arch.) | 14 nm | 11/2019 | 18C |  | DDR4-2933 | 48 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 165 W | LGA 066

## Slide 184: 4. Evolution of HEDT (High-End Desktop) processors (29)
What is the outlook of HEDT processors?
The performance of DT processors rose very dynamically, e.g., Intel’s 13th gen.
DT processors already have 24 cores and have achieved 6.0 GHz boost frequencies
while they cost considerably less than HEDT processors.
Presumably, this is the main reason why neither Intel nor AMD upgraded their
HEDT lines since 2019.
As a consequence, due to dwindling demand and lack of new, upgraded HEDT lines,
the HEDT market has crashed in the years 2019-2022, as sales statistics from
the USA indicates it (see the following Figure).

## Slide 185: 4. Evolution of HEDT (High-End Desktop) processors (30)
Dwindling sales figures of HEDT processors in the years 2020-2022, as stated
by a leading US supplier of workstations (2020-2022) [56]
Above sales figures indicate, that the HEDT market collapsed between 2020 and 2022
due to the reasons mentioned.
Consequently, HEDT processors seem to disappear from the processor market.

## Slide 186
5. Evolution of high-end 2S server processors
Notes: 186

## Slide 187: 5. Evolution of high-end 2S server processors (1)
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smarphones
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smartphones
Desktops
Servers
Recent major processor categories of Intel
Xeon E7/E5/E3
Platinum/Gold etc.
Clients
(Desktops/Laptops)
Core i9/i7/i5/i3
(Basic architectures)
HEDTs
(High-End Desktops)
Core i7/i9
(Extreme Edition
or X models)
5. Evolution of high-end 2S server processors -1
Mobiles
(Tablets/Smartphones)
Atom lines
Atom lines
(+ LP Core models)

## Slide 188: 5. Evolution of high-end 2S server processors (2)
Evolution of high-end 2S server processors -2
After an introduction, in this Section we are concerned with the following questions:
Are Intel’s server processors built up monolithic or multi-die designs?
How large are Intel’s 2S server dies, and how many transistors do they include?
At what rate could core counts and memory speeds be raised in Intel’s high-end
Core 2-based 2S server processors?
What are the implications if memory rates rise slower than core counts
over server generations?
What power consumption have Intel’s 2S server processors (in terms of TDP)
and how they are socketed.

## Slide 189: 5. Evolution of high-end 2S server processors (3)
A straightforward classification of server platforms that is based on
the number of sockets included
2S (DP)
server platforms
Server platforms
Platforms for more than 8 sockets
2- processor server platforms
(2-socket server platforms)
4S/8S (MP)
server platforms
4/8-processor server platforms
(4/8-socket server platforms)
Server platforms for
more than the Intel
supported number of
sockets
(4 or 8 sockets)
They need third party
node controllers
Uniprocessor server platforms
(UP-server platforms)
1-processor server platforms
(1-socket server platforms)
Multiprocessor server platforms
Server platforms supporting more than one processor
(Multi-socket server platforms)
S: Socket
DP: Dual Processor
MP: Multi-Processor
Note that the terms “processor” and “socket” are synonyms in connection with servers.
From the above alternatives, this Section is concerned only with 2S server processors since they
dominate the server market, as the following Figure indicates.

## Slide 190: 5. Evolution of high-end 2S server processors (4)
2016 market share of 1S/2S/4S servers (number of units sold) [27]
As seen, in 2016, 2S servers dominated the server market by far (by about 80%).
A similar market share may be expected recently as well.

## Slide 191: 5. Evolution of high-end 2S server processors (5)
Platform | HE multicore 2S server models | Techn. | Date of Intro. | Core count (up to) | PCIe | No./speed of mem. channels per socket (up to) | TDP (up to) W | Socket
Bensley | Xeon 5000 (Dempsey) (P4 Prescott 2M DP) | 65 nm | 5/2006 | 2x1C | 16x PCIe 1.0 (on MCH) | 4x DDR2-533 (FB-DIMM) | 130 | LGA 771
 | Xeon 5100 (Woodcrest) (Core 2) | 65 nm | 6/2006 | 2C | 16x PCIe 1.0 (on MCH) | 4x DDR2-667 (FB-DIMM) | 65 | LGA 771
 | Xeon 5300 (Clovertown) (Core 2) | 65 nm | 11/2006 | 2x2C | 16x PCIe 1.0 (on MCH) | 4x DDR2-667 (FB-DIMM) | 80 | LGA 771
 | Xeon 5400 (Harpertown) (Penryn) | 45 nm | 11/2007 | 2C | 24x PCIe 1.0 (on MCH) | 4x DDR2-667 (FB-DIMM) | 120 | LGA 771
Tylersburg | Xeon E55xx (Nehalem–EP) Gainestown) | 45 nm | 3/2009 | 4C | 36x PCIe 2.0 (on MCH) | 3x DDR3-1333 | 95 | LGA 1366
Boxboro-EX | Xeon E65xx Nehalem-EX) (Beckton) | 45 nm | 3/2010 | 8C | 36x PCIe 2.0 (on MCH) | 8x DDR3-1066 | 130 | LGA 1567
 | Xeon E7-28xx (Westmere-EX) | 32 nm | 4/2011 | 10C |  | 8x DDR3-1333 | 130 | 
Brickland | E7-28xx v2 (Ivy Bridge-EX) | 22 nm | 2/2014 | 15C | 32x PCIe 3.0 (on proc.) | 8x DDR3-1600 | 155 | LGA 2011-1
Grantley | E5-26xx v3 (Haswell-EP) | 22 nm | 9/2014 | 18C | 40x PCIe 3.0 (on proc.) | 4x DDR4-2133 | 160 | LGA 2011-3
 | E5-26xx v4 (Broadwell-EP) | 14 nm | 4/2016 | 22C |  | 4x DDR4-2400 | 300 | 
Overview of Intel’s earlier 64-bit multicore high-end 2S server processors

## Slide 192: 5. Evolution of high-end 2S server processors (6)
Platform | HE multicore 2S server models | Techn. | Date of Intro. | Core count (up to) | PCIe | No./speed of mem. channels per socket (up to) | TDP (up to) W | Socket
Purley | Xeon Platinum 8176/8180 (Skylake-SP) | 14 nm | 7/2017 | 28C | 48x PCIe 3.0 (on proc.) | 6x DDR4-2400 | 105 | LGA 3647
 | Xeon Platinum 8276/80 (Cascade Lake-SP) | 14 nm | 4/2019 | 28C | 48x PCIe 3.0 (on proc.) | 6x DDR4-2400 | 205 | 
 | Platinum 9282 (Cascade Lake-AP) | 14 nm | 4/2019 | 2x28 | 40x PCIe 3.0 (on proc.) | 12x DDR4-2933 | 400 | BGA 5903
 | Xeon Gold 6238R/58R (Cascade Lake-SP) | 14 nm | 2/2020 | 28C | 48x PCIe 3.0 (on proc.) | 6x DDR4-2933 | 205 | LGA 3647
Whitley | Xeon Platinum 8380 Eis Lake-SP | 10 nm | 4/2021 | 40C | 64xPCIe4.0 (on proc) | 8x DDR4-3200 | 270 | LGA 4189
Eagle Stream | Xeon Platinum 8490H Sapphire Rapid | Intel 7 | 1/2023 | 60C | 80xPCIe5.0 (on proc.) | 8x DDR5-4800 | 350 | LGA 4677
 | Emerald Rapid | Intel 7 | 2024 | 64C? | 80xPCIe5.0 (on proc) | 8x DDR5-4800 | n.a. | 
Overview of Intel’s recent scalable 64-bit multicore high-end 2S server processors
Remarks
Intel introduced the scalable term in 2017 (along with the Skylake-SP-based (Purely
platform) for platforms and processors with a unified design for all performance classes
(e.g., high-performance and efficient classes) and socket counts from 2 to 8.
Intel’s Copper Lake processors (14 nm, 28C), launched in 6/2020 are not included
in the above Table since they only aim at 4S/8S servers.

## Slide 193: 5. Evolution of high-end 2S server processors (7)
Are Intel’s server processors monolithic- or multi-die designs? -1
early dual die processor designs
the dual-die 56-core Cascade Lake 9200-AP processor (2019) and
high core count four-die Sapphire Rapid processor designs (2023),
as briefly discussed next.
Until now Intel mostly rolled out monolithic server processors, with three exceptions:

## Slide 194: 5. Evolution of high-end 2S server processors (8)
a) Early dual-die processor designs
Paxville DP 2.8: (2x1C), 2xDP-enhanced 64-bit Pentium 4 Prescott (10/2005)
Xeon 5000 (Dempsey): (2x1C), ~ the 65 nm shrink of the 90 nm Paxville DP 2.8 (5/2006)
Example: The 4-core
Xeon 5300
implemented on two dies
(Clowertown) [4], [5]
Xeon 5300 (Clowertown): (2x2C) 2x Core 2-based 65 nm Xeon 5100 (Woodcrest), 11/2006
Xeon 5400 Harpertown: (2x2C), 2x Core 2-based 45 nm 2C Harpertown (11/2007)
About 2005, in the dawn of the multiprocessor era, Intel speeded up their appearance
into this advanced field by implementing certain Pentium 4 or Core 2-based dual- or
quad-core server processors on two dies, properly interconnected, rather than waiting
for later monolithic implementations, as shown below.

## Slide 195: 5. Evolution of high-end 2S server processors (9)
b) The dual-die 56-core Cascade Lake 9200-AP processor (2019)
The Cascade Lake 9200-AP is implemented on two Cascade Lake-SP dies
properly interconnected (presumable by a UPI bus) and enclosed into a BGA
(Ball Grid Array) package, as indicated in the Figure below.
Figure: Dual-chip module of the 9200-AP [28]
This design was spurred by AMD’s 64-bit Zen-based server processors, since
at that time, Intel offered only up to 28-core designs.
We note that the 9200-AP was sold for OEMs, as it was BGA packaged and had to
to be surface mounted (soldered) onto the mainboard rather than to be inserted
into a socket.
OEM: Original Equipment Manufacturer (like Dell, hp etc.)

## Slide 196: 5. Evolution of high-end 2S server processors (10)
c) The high core count four-die Sapphire Rapid processor design (2023) -1
Figure: 15-core
die of a four-die
Sapphire Rapids
Processor [57]
The Sapphire Rapids line is built up on either a single die or quad dies.
All high core count models (nc > 32) are implemented on quad-dies, but there are
also lower core count four-die implementations.
In the four-die configuration a single die includes up to 15 CPU cores, a 128-bit
DDR5 memory interface and further units, as seen in the Figure below.
EMIB: embedded
Multi-Die Interconnect
Bridge (2D interconnect)

## Slide 197: 5. Evolution of high-end 2S server processors (11)
The Figure below shows single- and quad-die implementations of Sapphire Rapids
processors.
Figure: Die configurations of Sapphire Rapids processors.
c) The high core count four-die Sapphire Rapid processor design (2023) -2
Note that all die configurations provide 4x128-bit DDR5 interfaces (equaling 8x64-bit
memory channels).
Multiple dies are interconnected by Intel’s 2D EMIB technology.
(with HBM, max. 56 cores)
(max. 60 cores)
(max. 32 cores)

## Slide 198: 5. Evolution of high-end 2S server processors (12)
Intel’s vision of the Open Chiplet (multivendor) platform on a package
As seen in the Figure, in the future, Intel expects platforms consisting of multiple chiplets
from multiple vendors, interconnected by a universal UCIe interconnect express bus
and encased by an advanced packaging technique. [58]

## Slide 199: 5. Evolution of high-end 2S server processors (13)
HCC (XCC) layout
(High/Extreme Core Count)
for up to 15 cores
MCC layout
(Medium Core Count)
for up to 10 cores
LCC layout
(Low Core Count)
for up to 6 cores
Figure: Three monolithic die layouts of the Ivy Bridge-EX line (2014) [59]
Intel’s implementation of monolithic dies
All of Intel’s early, previously not mentioned server processors with up to 10 cores
are implemented monolithically on a single die.
If then specific models provided fewer cores than the max. core count implemented
on the die, only the stated number of cores are activated (e.g., 4 or 6 from 10).
Subsequently, beginning with the up to 15-core Ivy Bridge-EX (2014) line, Intel
began to optimize the fabrication costs of their processors by using three
die layouts (as, e.g. depicted below) and choosing the appropriate die layout for
implementing their processor models.

## Slide 200: 5. Evolution of high-end 2S server processors (14)
Platform4 | Core | Techn. | Intro. | High performance Core 2-based multicore 2S server processors | Core count up to | Trans. count [106/109] | Die size [mm2]
Bensley | Pentium 4 Prescott 2M DP | 65 nm | 5/2006 | Xeon 5000 (Dempsey) | 2x1C | 2x188 | 2x81
 | Core2 | 65 nm | 6/2006 | Xeon 5100 (Woodcrest) | 2C | 291 | 143
 | Core2 | 65 nm | 11/2006 | Xeon 5300 (Clovertown) | 2x2C | 2x291 | 2x143
 | Penryn | 45 nm | 11/2007 | Xeon 5400 (Harpertown) | 2x2C | 2x410 | 2x107
Boxboro-EX | Nehalem | 45 nm | 3/2010 | Xeon X6500 (Beckton/Nehalem-EX) | 8C | 2.3 | 513
 | Westmere | 32 nm | 4/2011 | Xeon E7-28xx (Westmere-EX) | 10C | 2.6 | 512
Brickland | Ivy Bridge | 22 nm | 2/2014 | Xeon E7-28xx v2 (Ivy Bridge-EX) | 15C | 4.31 | 541
 | Haswell | 22 nm | 9/2014 | Xeon E5-2600xx v3 (Haswell-EP) | 18C | 5.69 | 662
 | Broadwell | 14 nm | 4/2016 | Xeon E5-26xx v4 (Broadwell-EP) | 22C | 7.2 | 456
Purley | Skylake | 14 nm | 7/2017 | Xeon Platinum 8176/80 (Skylake-SP) | 28C | 8.0? | ~678
 | Cascade Lake | 14 nm | 4/2019 | Xeon Platinum 8276/80 (Cascade Lake-SP) | 28C | n.a. | n.a.
 | Cascade Lake | 14 nm | 4/2019 | Xeon Platinum 9282 (Cascade Lake-AP) | 2x28C | n.a. | n.a.
 | Cascade Lake R | 14 nm | 2/2020 | Xeon Gold 6238R/6258 (Cascade Lake R) | 28C | n.a. | n.a.
Whitney | Ice Lake | 10 nm | 4/2020 | Xeon Platinum 8380 (Ice Lake-SP) | 40C | n.a. | ~640
Eagle Stream | Sapphire Rapids | Intel 7 | 1/2023 | Xeon Sapphire Rapids MCC monolithic die | 32C | n.a. | ~770
 | Esmerald Rapids | Intel 7 | 2024 |  | 64C |  | 
How large are Intel’s server dies? -1
The Table below shows related data.

## Slide 201: 5. Evolution of high-end 2S server processors (15)
How large are Intel’s 2S server dies -2
As the previous Table indicates, initially, Intel dynamically enlarged the die sizes of their
server processors, but after having achieved 600-700 mm2 (6-7 cm2), die sizes
did not grow notably anymore.
There are two reasons for this: mask alignment problems and the rising defect
numbers that reduce die yields.
At present, Intel’s largest die seems to be the Sapphire Rapids 32-core MCC die,
measuring about 770 mm2.
By contrast, Intel’s Sapphire Rapids XCC dies measure 400 mm2, i.e., their 4-die
processors have a total silicon area of about 1600 mm2 (16 cm2) [60].

## Slide 202: 5. Evolution of high-end 2S server processors (16)
How many transistors Intel’s 2S server dies include? -1
Up to the Skylake family (2017), Intel revealed die sizes and transistor counts, but
after that, sorry to say, the firm has stopped stating related data, so for recent
processors, no reliable data is available.

## Slide 203: 5. Evolution of high-end 2S server processors (16b)
Platform4 | Core | Techn. | Intro. | High performance Core 2-based multicore 2S server processors | Core count up to | Trans. count [106/109] | Die size [mm2]
Bensley | Pentium 4 Prescott 2M DP | 65 nm | 5/2006 | Xeon 5000 (Dempsey) | 2x1C | 2x188 | 2x81
 | Core2 | 65 nm | 6/2006 | Xeon 5100 (Woodcrest) | 2C | 291 | 143
 | Core2 | 65 nm | 11/2006 | Xeon 5300 (Clovertown) | 2x2C | 2x291 | 2x143
 | Penryn | 45 nm | 11/2007 | Xeon 5400 (Harpertown) | 2x2C | 2x410 | 2x107
Boxboro-EX | Nehalem | 45 nm | 3/2010 | Xeon X6500 (Beckton/Nehalem-EX) | 8C | 2.3 | 513
 | Westmere | 32 nm | 4/2011 | Xeon E7-28xx (Westmere-EX) | 10C | 2.6 | 512
Brickland | Ivy Bridge | 22 nm | 2/2014 | Xeon E7-28xx v2 (Ivy Bridge-EX) | 15C | 4.31 | 541
 | Haswell | 22 nm | 9/2014 | Xeon E5-2600xx v3 (Haswell-EP) | 18C | 5.69 | 662
 | Broadwell | 14 nm | 4/2016 | Xeon E5-26xx v4 (Broadwell-EP) | 22C | 7.2 | 456
Purley | Skylake | 14 nm | 7/2017 | Xeon Platinum 8176/80 (Skylake-SP) | 28C | 8.0? | ~678
 | Cascade Lake | 14 nm | 4/2019 | Xeon Platinum 8276/80 (Cascade Lake-SP) | 28C | n.a. | n.a.
 | Cascade Lake | 14 nm | 4/2019 | Xeon Platinum 9282 (Cascade Lake-AP) | 2x28C | n.a. | n.a.
 | Cascade Lake R | 14 nm | 2/2020 | Xeon Gold 6238R/6258 (Cascade Lake R) | 28C | n.a. | n.a.
Whitney | Ice Lake | 10 nm | 4/2020 | Xeon Platinum 8380 (Ice Lake-SP) | 40C | n.a. | ~640
Eagle Stream | Sapphire Rapids | Intel 7 | 1/2023 | Xeon Sapphire Rapids MCC monolithic die | 32C | n.a. | ~770
 | Esmerald Rapids | Intel 7 | 2024 |  | 64C |  | 
How many transistors Intel’s 2S server dies include? -2
The Table below shows related data.

## Slide 204: 5. Evolution of high-end 2S server processors (16c)
How many transistors Intel’s 2S server dies include? -3
Nevertheless, one of the Figures in Section 1 shows transistor densities in recent
IC processes.
Accordingly, Intel7 technology yields about 180 million transistors/mm2.
It follows that Intel’s most giant, 32-core Sapphire Rapids MCC die (measuring 770 mm2)
may have nearly 140 billion transistors (note that due to the unknown size of
“dark silicon,” the actual transistor count implemented on the die, may be estimated
only very roughly).
Dark silicon: unoccupied Si area.

## Slide 205: 5. Evolution of high-end 2S server processors (17)
At what rate do transistor counts rise in Intel’s 2S server processors? -1
Related data of the previous Table allows to visualize the rate of rising transistor counts
as follows:

## Slide 206: 5. Evolution of high-end 2S server processors (18)
Core count
2006
2008
2010
2012
2014
2016
Year
Nehalem-EX
(45 nm)
Westmere-EX
(32 nm)
Ivy-Bridge-EX
(22 nm)
Broadwell-EP
(14 nm)
*
*
*
*
2
4
8
18
28
22
10
6
15
*
*
~2x/4 years
Emergence of
L3 caches in Core 2-based
high-end 2S processors
*
Haswell-EP
(22 nm)
12
2018
56
*
Cascade Lake-AP
(Two dies)
(14 nm)
2020
40
*
*
Skylake-SP
(14 nm)
*
Cascade Lake-SP
(14 nm)
Ice Lake-SP
(10 nm)
~2x/2 years
*
5100
(Core 2-based)
(65 nm)
Two-die
implementations
5400
(Penryn b.)
(45 nm)
5300
(Core 2 b.)
(65 nm)
b.: based HE: High-End
60
2022
*
Copper Lake
(Intel 7)
~2x/4 years
*
P4 2M DP
(65 nm)
At what rate do core counts rise in Intel’s 2S server processors? -2

## Slide 207: 5. Evolution of high-end 2S server processors (23)
At what rate could core counts be raised in Intel’s high-end Core 2-based 2S
server processors ? -3
As the above graph indicates, Intel raised the core count of their 2S server processors
at two different rates, as discussed subsequently:

## Slide 208: 5. Evolution of high-end 2S server processors (24)
Doubling core counts in two years in L3-less high-end Core 2-based 2S
server processors -1
Core count
2006
2008
2010
2012
2014
2016
Year
Nehalem-EX
(45 nm)
Westmere-EX
(32 nm)
Ivy-Bridge-EX
(22 nm)
Broadwell-EP
(14 nm)
*
*
*
*
2
4
8
18
28
22
10
6
15
*
*
~2x/4 years
Emergence of
L3 caches in Core 2-based
high-end 2S processor lines
*
Haswell-EP
(22 nm)
12
2018
56
*
Cascade Lake-AP
(Two dies)
(14 nm)
2020
40
*
*
Skylake-SP
(14 nm)
*
Cascade Lake-SP
(14 nm)
Ice Lake-SP
(10 nm)
~2x/2 years
*
5100
(Core 2-based)
(65 nm)
Two-die
implementations
5400
(Penryn b.)
(45 nm)
5300
(Core 2 b.)
(65 nm)
b.: based HE: High-End
60
2022
*
Copper Lake
(Intel 7)
~2x/4 years
*
P4 2M DP
(65 nm)

## Slide 209: 5. Evolution of high-end 2S server processors (25)
Doubling core counts in two years in L3-less high-end Core 2-based 2S server processors -2
In the first phase of the evolution, core counts of Core 2-based 2S servers needed
two years to double, as indicated in the previous Figure.
This seems quite evident in light of Moore’s rule since doubling transistor
counts every two years will also allow doubling core counts.
This evolution, however, ended when L3 caches appeared, and the rate of rising
core counts slowed (see the following Figure).

## Slide 210: 5. Evolution of high-end 2S server processors (26)
b) Slowing down the growth rate of core counts in high-end 2S server processors
after L3 caches emerged -1
Core count
2006
2008
2010
2012
2014
2016
Year
Nehalem-EX
(45 nm)
Westmere-EX
(32 nm)
Ivy-Bridge-EX
(22 nm)
Broadwell-EP
(14 nm)
*
*
*
*
2
4
8
18
28
22
10
6
15
*
*
~2x/4 years
Emergence of
L3 caches in Core 2-based
high-end 2S processors
*
Haswell-EP
(22 nm)
12
2018
56
*
Cascade Lake-AP
(Two dies)
(14 nm)
2020
40
*
*
Skylake-SP
(14 nm)
*
Cascade Lake-SP
(14 nm)
Ice Lake-SP
(10 nm)
~2x/2 years
*
5100
(Core 2-based)
(65 nm)
Two-die
implementations
5400
(Penryn b.)
(45 nm)
5300
(Core 2 b.)
(65 nm)
b.: based HE: High-End
60
2022
*
Copper Lake
(Intel 7)
~2x/4 years
*
P4 2M DP
(65 nm)

## Slide 211: 5. Evolution of high-end 2S server processors (27)
b) Slowing down the growth rate of core counts in high-end 2S server processors
after L3 caches emerged -2
As seen in the previous Figure, after L3 caches emerged, core counts’ evolution
slowed down to a rate of doubling approximately every four years.
This change is in harmony with the reduced rate of rising transistor counts,
discussed earlier.

## Slide 212: 5. Evolution of high-end 2S server processors (28)
c) Delay in raising core counts due to difficulties Intel met in their IC fabrication -1
On their way to the 10 nm technology Intel encountered unexpected difficulties
that interrupted the rise of core counts for about two years, as the next Figure
depicts.

## Slide 213: 5. Evolution of high-end 2S server processors (29)
c) Delay in raising core counts due to Intel’s IC fabrication difficulties -1
Core count
2006
2008
2010
2012
2014
2016
Year
Nehalem-EX
(45 nm)
Westmere-EX
(32 nm)
Ivy-Bridge-EX
(22 nm)
Broadwell-EP
(14 nm)
*
*
*
*
*
2
4
8
18
28
22
10
6
15
*
*
~2x/4 years
Emergence of
L3 caches in Core 2-based
high-end 2S processor lines
*
Haswell-EP
(22 nm)
12
2018
56
*
Cascade Lake-AP
(Two dies)
(14 nm)
2020
40
*
*
Skylake-SP
Platinum/Gold
(14 nm)
*
Cascade Lake-SP
Platinum/Gold
(14 nm)
Ice Lake-SP
(10 nm)
~2x/2 years
*
5100
(Core 2-based)
(65 nm)
Two-die
implementations
5400
(Penryn b.)
(45 nm)
5300
(Core 2 b.)
(65 nm)
DP 2.8 GHz
(Pentium 4 b.)
(90 nm)

## Slide 214: 5. Evolution of high-end 2S server processors (30)
How far memory speeds could follow the dynamic rise of core counts
in Intel’s 2S HE server processors -1
In order to discuss this point, let’s inspect how fast memory speeds have been raised
in Intel’s 2S high-end server processors (see the following Figure).

## Slide 215: 5. Evolution of high-end 2S server processors (3118)
The rate of rising memory speeds in Intel’s 2S HE server processors
Transfer rate
(MT/s)
50
100
500
Year
05
2004
06
07
08
1000
3000
200
2000
~ 2*/4 years
09
11
2010
12
13
15
DDR3
1067

14
~ 2*/8 years
x
x
x
x
DDR
400
DDR2
667
DDR3
1600
2S
Emergence of
DDR3 memory
16
17
x
DDR4
2400
DDR4
2933
Emergence of
DDR4 memory
19
18
2020
DDR3
1333
x
x
x
DDR4
2666
DDR4
3200
x
22
21
5000
x
DDR5
4800
Emergence of
DDR5 memory

## Slide 216: 5. Evolution of high-end 2S server processors (32)
How far memory speeds could follow the dynamic rise of core counts
in Intel’s 2S HE server processors -2
As the above Figure shows, memory speeds has been raised in two different rates.
Initially, while using DDR and DDR2 memories, memory transfer rates were
doubled roughly in four years.
But after DDR3 memories emerged, the growth rate of memory transfer rates
slowed down to doubling roughly every eight years due to the higher complexity
of the technology.
When we compare at what rate core counts and memory speeds have been raised,
we find that memory transfer rates could be increased approximately at the
half rate compared to the rate of core counts in the considered time interval.

## Slide 217: 5. Evolution of high-end 2S server processors (33)
What are the implications when memory speeds rise slower than core counts
over server generations?
Let’s inspect how the per-core memory bandwidth (BWM/nC)
BWM/nC = nM ∗ w ∗ TM /nC
changes when memory transfer rates (TM) rise slower than core counts (nC),
(while the w, i.e., the width of the memory channels remains constant).
In this case, the ratio TM/nC will obviously be decreased since TM rises slower than
nC over processor generations.
As a consequence, less and less per core memory bandwidth (BWM/nC) would be
available; in other words, a memory bandwidth gap would arise unless adequate
countermeasures will take place.

## Slide 218: 5. Evolution of high-end 2S server processors (34)
How can the per-core memory bandwidth be preserved over generations
while memory transfer rates rise slower than core counts?
Assuming the same memory channel width (w), the per-core memory bandwidth
(BWM/core) can clearly be preserved when
nM ∗ TM /nC
remains constant, i.e., when the number of memory channels will be raised
appropriately.
BWM/nC = nM ∗ w ∗ TM /nC
Let’s consider again the expression of the per core memory bandwidth

## Slide 219: 5. Evolution of high-end 2S server processors (35)
How many memory channels (nM) are needed per socket for preserving
the per core memory bandwidth vs. a reference platform?
nC | nM
2 | 2.0
4 | 2.8
6 | 3.5
8 | 4.0
10 | 4.5
12 | 4.9
14 | 5.3
16 | 5.6
20 | 6.3
24 | 6.9
32 | 8.0
48 | 9.8
64 | 11.3
Table: Actual number of memory channels (nM)
needed per socket to preserve the per-core memory bandwidth of a high-end 2S server with nC cores
while a selected platform is taken as a reference
(and CPU cores as well as memory speeds
have raised at rates as discussed before)
The Table on the right shows how many memory
channels are needed per socket (nM) according
to the expression presented.
If core counts and memory speeds are rising over generations at rates as discussed,
a high-end 2S server with nC cores requires approximately
nM = √2 ∗ √n memory channels per socket for preserving
the per-core memory bandwidth vs. a selected reference platform, as stated in [29].
It follows e.g. that a 32-core processor needs
8 memory channels to preserve the per core
memory bandwidth per socket vs. the assumed
reference platform.

## Slide 220: 5. Evolution of high-end 2S server processors (36)
One of the key challenges in designing server processors -1
As subsequent processor families usually implement more and more cores, more
and more memory channels are needed as well to compensate for the fact that
memory speeds rise slower than core counts.
It is however, quite an intricate task to raise the number of memory channels due to
electrical and physical constraints, not discussed in this Chapter, so providing
enough memory channels, i.e., memory bandwidth per socket, is one of the key
challenges in designing server processors and platforms.
In the next Table we show how far Intel has succeeded to preserve per-core
memory bandwidth (relative to a chosen reference platform) in their high-end
2S server platforms by increasing the number of memory channels while raising
the core count of their server processors.

## Slide 221: 5. Evolution of high-end 2S server processors (37)
Platform 605 | 48re | Techn. | Date of Intro. | High-end multicore 2S server lines | Core count (up to) | Per socket mem. channels (up to) | Per core BW rel. to ref. platform
Ref. platform | Pentium 4 Prescott DP | 90 nm | 6/2004 | 90 nm Nocona | 1C | 1x DDR2/400 | 1.0
 | Pentium 4 Presc. | 90 nm | 10/2005 | Xeon DP 2.8 (Paxville DP) | 2x1C | 1x DDR2/400 | 0.5
Bensley | Pentium 4 Presc. | 65 nm | 5/2006 | Xeon 5000 (Dempsey) | 2x1C | 2x DDR2/667 | 1.7
 | Core2 | 65 nm | 6/2006 | Xeon 5100 (Woodcrest) | 2C | 2x DDR2/667 | 1.7
 | Core2 | 65 nm | 11/2006 | Xeon 5300 (Clowertown) | 2x2C | 2x DDR2/667 | 0.8
 | Penryn | 45 nm | 11/2007 | Xeon 5400 (Harpertown) | 2x2C | 2x DDR2/667 | 0.8
Tylersburg | Nehalem | 45 nm | 3/2009 | Xeon 55xx (Gainestown) | 4C | 3x DDR3/1333 | 2.5
Boxboro-EX | Nehalem | 45 nm | 3/2010 | Xeon X6500 Nehalem-EX) | 8C | 8x DDR3/1066 | 2.7
 | Westmere | 32 nm | 4/2011 | Xeon E7-28xx (Westmere-EX) | 10C | 8x DDR3/1333 | 2.7
Brickland | Ivy Bridge | 22 nm | 2/2014 | Xeon E7-28xx v2 (Ivy Bridge-EX) | 15C | 8x DDR3/1600 | 2.1
Grantley | Haswell | 22 nm | 9/2014 | Xeon E5-2600xx v3 (Haswell-EP) | 18C | 4x DDR4/2133 | 1.2
 | Broadwell | 14 nm | 4/2016 | Xeon E5-26xx v4 (Broadwell-EP) | 22C | 4x DDR4/2400 | 1.1
Purley | Skylake | 14 nm | 7/2017 | Xeon Platinum (8176/80 Skylake-SP) | 28C | 6x DDR4/2666 | 1,4
 | Cascade Lake | 14 nm | 4/2019 | Xeon Platinum 8276/80 (Cascade Lake-SP) | 28C | 6x DDR4/2933 | 1.6
Whitney | Ice Lake | 10 nm | 4/2021 | Xeon Platinum 8380 (Ice Lake-SP) | 40C | 8x DDR4-3200 | 1.6
Eagle Stream | Sapphire Rapid | Intel 7 | 1/2023 | Xeon Platinum 8490H (Sapphire Rapid) | 60C | 8x DDR5-4800 | 1.6
Achieved relative per core bandwidth in Intel’s high end 2S server platforms
1

## Slide 222: 5. Evolution of high-end 2S server processors (38)
As data in the previous Table indicates, Intel could preserve the per-core memory
bandwidth in their Core 2-based high-end 2S server processors relating to a
reference platform (identified by dark blue color), certainly with some differences,
yet provided in a few lines even higher bandwidth per core than expected by the
discussed relation.
How far Intel preserved the per core bandwidth in their HE 2S server processors?

## Slide 223: 5. Evolution of high-end 2S server processors (39)
What power consumption Intel’s 2S server processors have (in terms of TDP)
and how they are socketed? -1
Finally, the next Table gives an overview of the power consumption (in terms of the
TDP value) and socketing of Intel’s high-end 2S server processors.

## Slide 224: 5. Evolution of high-end 2S server processors (40)
Platform | HE multicore 2S server models | Techn. | Date of Intro. | Core count (up to) | PCIe | No./speed of mem. channels per socket (up to) | TDP (up to) W | Socket
Tylersburg | Xeon E55xx (Nehalem –EP) Gainestown) | 45 nm | 3/2009 | 4C | 36x PCIe 2.0 (on MCH) | 3x DDR3-1333 | 95 | LGA 1366
Boxboro-EX | Xeon E65xx Nehalem-EX) (Beckton) | 45 nm | 3/2010 | 8C | 36x PCIe 2.0 (on MCH) | 8x DDR3-1066 | 130 | LGA 1567
 | Xeon E7-28xx (Westmere-EX) | 32 nm | 4/2011 | 10C |  | 8x DDR3-1333 | 130 | 
Brickland | E7-28xx v2 (Ivy Bridge-EX) | 22 nm | 2/2014 | 15C | 32x PCIe 3.0 (on proc.) | 8x DDR3-1600 | 155 | LGA 2011-1
Grantley | E5-26xx v3 (Haswell-EP) | 22 nm | 9/2014 | 18C | 40x PCIe 3.0 (on proc.) | 4x DDR4-2133 | 160 | LGA 2011-3
 | E5-26xx v4 (Broadwell-EP) | 14 nm | 4/2016 | 22C |  | 4x DDR4-2400 | 300 | 
Purley | Xeon Platinum 8176/8180 (Skylake-SP) | 14 nm | 7/2017 | 28C | 48x PCIe 3.0 (on proc.) | 6x DDR4-2400 | 105 | LGA 3647
 | Xeon Platinum 8276/80 (Cascade Lake-SP) | 14 nm | 4/2019 | 28C | 48x PCIe 3.0 (on proc.) | 6x DDR4-2400 | 205 | 
 | Platinum 9282 (Cascade Lake-AP) | 14 nm | 4/2019 | 2x28 | 40x PCIe 3.0 (on proc.) | 12x DDR4-2933 | 400 | BGA 5903
 | Xeon Gold 6238R/58R (Cascade Lake-SP) | 14 nm | 2/2020 | 28C | 48x PCIe 3.0 (on proc.) | 6x DDR4-2933 | 205 | LGA 3647
Whitney | Xeon Platinum 8380 Eis Lake-SP | 10 nm | 4/2021 | 40C | 64x PCIe4.0 (on proc) | 8x DDR4-3200 | n.a. | LGA 4189
Eagle Stream | Xeon Platinum 8490H Sappire Lake | Intel 7 | 1/2023 | 60C | 80x PCIe5.0 (on proc) | 8x DDR5-4800 | 350 | LGA 4677
TDP values and socketing of Intel’s high-end NUMA 2S server processors

## Slide 225: 5. Evolution of high-end 2S server processors (41)
What power consumption Intel’s 2S server processors have (in terms of TDP)
and how they are socketed? -2
As the previous Table shows, high-end 2S server processors obviously have
considerably higher TDP values than typical desktop processors, ranging from 95 W
in early server processors up to 400 W in recent ones.
Note also that along with their evolution, 2S server processors need more and more
contacts on their sockets since subsequent server generations provide more
and more memory channels and PCIe lanes.
As an example, we mention that early 45-nm server processors had only 1366 contacts,
whereas 10 nm (Intel 7) Sapphire Lake server processors (2023) already need
much more, 4677 contacts.

## Slide 226
6. Evolution of mobile processors
Notes: 226

## Slide 227: 6. Evolution of mobile processors (1)
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smarphones
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smartphones
Desktops
Smarphones
Servers
Recent major processor categories of Intel
Atom lines
Xeon E7/E5/E3
Platinum/Gold etc.
Desktops/Laptops
(Clients)
Core i9/i7/i5/i3
(Basic architectures)
Atom lines
(+ LP Core models)
HEDTs
(High-End Desktops)
Core i7/i9
(Extreme Edition
or X models)
6. Evolution of mobile processors -1
Mobiles
(Tablets/Smartphones)
Remark
Both Intel and AMD designate laptop processors as mobile processors as well.

## Slide 228: 6. Evolution of mobile processors (2)
In this Section
Evolution of mobile processors -2
first, we point out the kind of requirements mobile processors impose,
then we discuss how far Intel’s and AMD’s traditional client processors were
suitable for mobile use,
next, we show how Intel and AMD responded to the challenges of the mobile era
and how successful their moves were,
finally, we show how far mobile processors have become wider and wider since
this aspect impacts the achievable performance very much.

## Slide 229: 6. Evolution of mobile processors (3)
6. Evolution of tablet and smartphone processors (2)
Why mobile processors evoke a new design paradigm?
As mobile devices require long operating hours, their advent (around 2000) evoke
a new design paradigm as well that aims at low power consumption rather than
at the highest performance churned out from a given power budget, as indicated below.
High performance/power
(e.g. GFLOPS/Watt)
Traditional processors
Tablets and smartphones
Low power
(Watt)
(Number of operating hours)

## Slide 230: 6. Evolution of mobile processors (4)
How early mobile processors achieved low power consumption?
Key features of early mobile processors
b) Low clock rates
a) Narrow CPU cores

## Slide 231: 6. Evolution of mobile processors (5)
a) Using narrow CPU cores in early mobile processors
Early smartphones emerged in the second half of the 2000’s and were mostly
based on ARM’s 32-bit wide Cortex processors.
Their CPUs were only 1-3 wide, as depicted in the following Figure.

## Slide 232: 6. Evolution of mobile processors (6)
2005
2007
2010
2009
(A9 replacement
for low-end
devices)
32-bit
Width of ARM’s 32-bit CPUs used in most early tablets and smartphones [30]
As seen, ARM’s early Cortex CPUs were 1-3 wide, constrained by the width of their decoders.
(The width of a CPU states the max. number of instructions that may flow through it per cycle).

## Slide 233
6. Evolution of mobile processors (7)
b) Applying low clock rates in early mobile processors
Power consumption = Active power: Dd = Cdyn∗VCC2 ∗ fc + Leakage power: Ds = VCC ∗ Ileak
Let’s first consider the basics of power consumption of CPUs.
Figure: Example: Core voltage (VCC) vs. clock frequency (fC) for Intel’s
Westmere processor models [32]
While higher fC requires higher VCC (VCC ≈ const x fC), as indicated below.

## Slide 234: 6. Evolution of mobile processors (8)
Relative high base frequency
(typically 2-4 GHz)
Client CPUs
Mobile CPUs
Relative low base frequency
(typically 1.5 -2.5 GHz)
Allow lower power budget
Allow higher power budget
How far TDP limits clock frequency (fc)?
As Dd = const x Vcc2 ∗ fc and Vcc = const ∗ fc, it follows that
Dd = const ∗ fc3
This means that dynamic dissipation rises very vital with the clock frequency,
in fact, it increases proportionally to the third power of fc.
As a consequence, the available power budget of the processors (usually given
in terms of their TDP), limits their base frequency, as indicated below.

## Slide 235
TDP (W) | No. of cores | Graphics | No. of graphics EUs | eDRAM | Base frequency (GHz)
4.5 | 2 | HD 515 | 18 | -- | 1.2
15 | 2 | HD 540 | 48 | 64 MB | 2.2
15 | 2 | HD 520 | 24 | -- | 2.6
28 | 2 | HD 550 | 48 | 64 MB | 3.3
35 | 4 | HD 530 | 24 | -- | 2.8
45 | 4 | HD 530 | 24 | -- | 2.9
65 | 4 | HD 530 | 24 | -- | 3.4
91 | 4 | -- | -- | -- | 4.2
Example for restricting the max. clock frequency by the TDP value
in Skylake desktop models of the Core 2 family (Based on data from [33])
6. Evolution of mobile processors (9)
As data in the Table shows, for example 4.5 W TDP limits the base frequency
to 1.2 GHz, whereas 91 W TDP allows a notable higher base frequency of 4.2 GHz.

## Slide 236: 6. Evolution of mobile processors (10)
Typical clock rates of early mobile processors
The low power budget (TDP) of early mobile processors limited their base frequency
to about 1.0 to 2.0 GHz.

## Slide 237: 6. Evolution of mobile processors (11)
How far Intel’s and AMD’s traditional processors were suited to mobile use? -1
This question may be answered by contrasting Intel’s and AMD’s CPU cores with ARM’s
early Cortex cores used at the down of the mobile era to power smartphones and tablets.
ARM’s early Cortex cores powering smartphones and tablets around 2006-2010 were typically
2-wide, 32-bit low-power designs, by contrast
traditional client processors were 4-wide 64-bit Intel designs (as the Figure below shows) or
3-wide, 64-bit AMD designs, both laid out for maximum performance/power
(in terms of GFLOPS/Watt).
Figure: Width of Intel’s Core 2 to Haswell processor cores
powering clients to servers [30]
(2006-2013)

## Slide 238: 6. Evolution of mobile processors (12)
As a consequence, both Intel and AMD were forced to design and introduce new,
narrow (e.g., 2-wide) low-power microarchitectures to successfully compete
in the mobile market space.
Due to their wider CPUs and different design orientations, Intel’s and AMD’s client
processors consumed much more power than ARM’s Cortex-processors, so they
were not well suited for mobile devices.
How far Intel’s and AMD’s traditional processors were suited to mobile use? -2

## Slide 239: 6. Evolution of mobile processors (13)
How Intel responded to the mobile challenge?
Intel’s response to the mobile challenge was their 2-wide (64-bit) Atom line,
introduced in 2008, as seen below.

## Slide 240: 6. Evolution of mobile processors (14)
Emergence of Intel’s Atom line aiming for tablets and smartphones (Based on [31])
2008
2-wide
in-order
4-wide
out-of-order
2-wide
in order
2-wide
out-of-order
2-wide
in-order
2-wide
out-of-order
2-wide
out-of-order
3-wide
out-of-order
5
Note that first implementations of the Atom family were 2-wide designs.

## Slide 241: 6. Evolution of mobile processors (15)
The tale of Intel’s Atom line
Note that these platforms included discrete modems, termed by XMM (except late
but canceled implementations), whereas most competing platforms (except
Apple’s ones) had already integrated modems.
Based on their Atom line Intel developed a large number of smartphones and
tablet platforms to gain a respectable market share in the mobile space as
shown, for example, in the following Figure.

## Slide 242: 6. Evolution of mobile processors (16)
The plethora of Intel’s Atom-based smartphone platforms (based on [34])
Eul H., & Bell M., Mobile at Intel, Investor Meeting 2012, Intel,
http://www.cnx-software.com/pdf/Intel_2012/2012_Intel_Investor_Meeting_Eul_Bell.pdf
Clover Trail+
(2013)
Medfield
(2012)
Merrifield
(2014)
Moorefield
(2014)
Lexington
(2013)
Slayton
(2014)
Z2520-2580
2x Saltwell
32 nm
+XMM 6268/6360/7160
Z2420
1x Saltwell
32 nm
+XMM 6265
Z2460/2480
1x Saltwell
32 nm
+XMM 6260
Z34x0
2x Silvermont
22 nm
+XMM 7160/7260
Z3xxx
2x Silvermont
22 nm
+A-GOLD 620
Z35xx
4x Silvermont
22 nm
+XMM 7260/2/35
Performance (not to scale)
Morestown
(2010)
Z6xx
1x Bonnell
45 nm
+Wireless
module
Riverton
(2015)
SoFIA
(x3 3G/LTE)
(2015)
Z3xxx
2x Airmont
14 nm
Integrated
LTE modem
C31xx/32xx/34xx
2x/4x Silvermont
28 nm
Integrated LTE
3G/4G modem
Planned, not mplemented
Cancelled
in 04/2016
Planned, not implemented
Morganfield
(2016)
Z5xxx
4x Goldmont
14 nm
+XMM 7360
Cancelled
in 04/2016

## Slide 243: 6. Evolution of mobile processors (17)
Intel’s effort to optimize their platforms from the software point of view
In their 2012 Investor meeting (5/2012), Intel revealed that more than 3000
engineers are working on OS support, among them about 1200 engineers
are dedicated alone to Android, as indicated below [35].

## Slide 244: 6. Evolution of mobile processors (18)
How much market share could Intel achieve for their smartphone- and tablet
application processors in 2015? (based on revenue) [36]
Smartphone application processors worldwide market share 2015 (revenue) | 
Qualcomm (USA) | 42 %
Apple (USA) | 21 %
MediaTek (Taiwan) | 19 %
Samsung (S. Korea) | 
Spreadtrum (China) | 
Tablet application processors worldwide market share 2015 (revenue) | 
Apple (USA) | 31 %
Qualcomm (USA) | 16 %
Intel (USA) | 14 %
MediaTek (Taiwan) | 
Samsung (S. Korea) | 
[Source: Related press releases of Strategy Analytics]
As the Table on the left indicates, in 2015 Intel did not achieve any notable market share
for their smartphone application processors.
Nevertheless, the Table on the right shows that Intel reached at this time a 14 %
market share for tablet processors, attained by paying subsidies for OEMs
(~ 50 $ /processor) to spurn a transition from ARM to Atom products.

## Slide 245: 6. Evolution of mobile processors (19)
Intel's losses suffered on mobile devices in 2013 - 2014 [37]
Owing to subsidies paid to OEMs, Intel's mobile and communication division lost
7 billion $ in the years 2013-2014, as indicated in the following Figure [38].
Figure: Revenues/operating income of Intel's Mobile and Communications segment
2013-2014 [38]

## Slide 246: 6. Evolution of mobile processors (20)
Intel's withdrawal from the smartphone and mobil market [39]
"I can confirm that the changes included canceling the Broxton platform as well as
SoFIA 3GX, SoFIA LTE, and SoFIA LTE2 commercial platforms to enable us to move resources to products that deliver higher returns and advance our strategy.
These changes are effective immediately.“ (As indicated in the next Figure).
Intel's statement says:
Due to their high losses, Intel first ceased paying subsidies, and then in 4/2016
announced their withdrawal from the mobile market.

## Slide 247: 6. Evolution of mobile processors (21)
Cancellation of Intel’s Atom-based smartphone platforms in 2016 (based on [40])
Eul H., & Bell M., Mobile at Intel, Investor Meeting 2012, Intel,
http://www.cnx-software.com/pdf/Intel_2012/2012_Intel_Investor_Meeting_Eul_Bell.pdf
Clover Trail+
(2013)
Medfield
(2012)
Merrifield
(2014)
Moorefield
(2014)
Lexington
(2013)
Slayton
(2014)
Z2520-2580
2x Saltwell
32 nm
+XMM 6268/6360/7160
Z2420
1x Saltwell
32 nm
+XMM 6265
Z2460/2480
1x Saltwell
32 nm
+XMM 6260
Z34x0
2x Silvermont
22 nm
+XMM 7160/7260
Z3xxx
2x Silvermont
22 nm
+A-GOLD 620
Z35xx
4x Silvermont
22 nm
+XMM 7260/2/35
Performance (not to scale)
Morestown
(2010)
Z6xx
1x Bonnell
45 nm
+Wireless
module
Riverton
(2015)
SoFIA
(x3 3G/LTE)
(2015)
Z3xxx
2x Airmont
14 nm
Integrated
LTE modem
C31xx/32xx/34xx
2x/4x Silvermont
28 nm
Integrated LTE
3G/4G modem
Planned, not mplemented
Cancelled
in 04/2016
Planned, not implemented
Morganfield
(2016)
Z5xxx
4x Goldmont
14 nm
+XMM 7360
Cancelled
in 04/2016

## Slide 248: 6. Evolution of mobile processors (22)
Implication of Intel's withdrawal from the smartphone and mobil market [39]
While having left the mobile market, Intel laid off about 12000 employees (~ 11 %
of their workforce).

## Slide 249: 6. Evolution of mobile processors (23)
How AMD responded to the mobile challenge?
With a disastrous long delay of about 3-years also AMD appeared on the mobile
processor market with their Cat line in 2011, as the following Figure depicts.

## Slide 250: 6. Evolution of mobile processors (24)
2014
4/2014
2-wide
out-of-order
2-wide
out-of-order
2-wide
out-of-order
4-wide
out-of-order
Emergence of AMD's Cat line in 2011 aiming for tablets and smartphones

## Slide 251: 6. Evolution of mobile processors (25)
AMD’s related achievements and cancellation of their Cat line in 2015
After poor results earned on the mobile market, AMD also decided to cancel their
Cat line.
The last core of this line was the Puma+ core (launched in 6/2015.
Subsequently, there was no sign of continuing the Cat line.
Instead, AMD emphasized the Zen architecture that was launched in 2017.

## Slide 252: 6. Evolution of mobile processors (26)
Nvidia’s farewell from the smartphone and tablet market as well, in June 2016 [41]
Instead, NVIDIA became interested in designing in-car computers and car
infotainment systems beyond their traditional field of discrete GPU cards (dGPUs).
“We are no longer interested in that market”. He adds, “Anybody can build smartphones, and we’re happy to enjoy these devices, but we’ll let someone else build them”.
In 6/2016 (at Computex), NVIDIA's CEO J. Huang declared the firm's leaving the
smartphone and tablet market by saying:

## Slide 253: 6. Evolution of mobile processors (27)
How far mobile processors have subsequently been evolved?
Since Intel, AMD, and Nvidia left the mobile market, mobile processors evolved
tremendously, as discussed in the Chapter “ARM’s CPU core designs”.
Nevertheless, to give a glimpse of this enormous evolution, we point out just a
single aspect, showing in the following two Figures how wide mobile processors
became in the last couple of years.

## Slide 254: 6. Evolution of mobile processors (28)
Early evolution and width of mobile CPU cores
We note that certain early mobile processors were only 1-wide 32-bit designs, like
ARM’s 1176 used in Apple’s iPhone (2007) or
ARM’s Cortex-A5 (2009)
nevertheless, for better clarity, these processors are not indicated in the next
Figure.
ARM’s early mobile processors were 32-bit designs and usually 2- or 3-wide,
subsequent mobile processors first became 64-bit designs (since about 2012)
followed by an impressive widening of their microarchitecture, as indicated in the
following Figures.

## Slide 255: 6. Evolution of mobile processors (29)
3-wide
2-wide
4-wide
Width of mobile cores
(or of big cores of big.LITTLE or dynamIQ core clusters)
5-wide
ARM
v7 Cortex-A (2005-09)
(except 1-wide LP A5 (2009)
and 3-wide HP A15))
v7 HP Cortex-A15
(2010)
Intel
Atom family (2008-15)
AMD
Cat family (2011-2015)
Apple
v7 Cortex-A8 (2009)
v7 Swift (A6) (2012)
Qualcomm
v7 Scorpion
(S1-S3) (2007-10)
v7 Krait
(S4/S400/S60x/S80x)
(2012-14)
v8 Kryo/Kryo 280
(S820/821/835) (2015/2016/2017)
v8.2 Kryo 385
(S845) (2018)
Samsung
v8.0 M1 (2016)
(Exynos 8 Octa)
v8 M2 (2017)
(Exynos 9 Octa)
v8.0 HP Cortex-A (2013-15) (except 2-wide HP Cortex-A73)
v7 Exynos 5
(2013-14)
v8 Exynos 7
(2016)
v8.2 HP Cortex-A76
(2018) to
HP Cortex-A78
(2020)
HP: High-Performance/big core
LP: Low-Power
v8.0 HP Cortex-A73
(2016)
Airmont-based Atom core (2016)
v8.0/8.2 LP Cortex-A
(2013/2017)
v8.2 HP Cortex-A75
(2017)
v8.2 HP Cortex-X1
(2020))
Widening of mobile CPU cores during their evolution -1

## Slide 256: 6. Evolution of mobile processors (30)
6-wide
7-wide
Width of mobile cores
(or of big cores of big.LITTLE or dynamIQ core clusters)
8-wide
ARM
Intel
AMD
Apple
Qualcomm
Samsung
HP: High-Performance/big core
LP: Low-Power
v8.0 HP A7-A10X
(2013-2017)
v8.2 HP A11 (2017)
v8.3 HP A12/A12X
(2018)
v8.4 HP A13 (2019)
v8.6 HP A14/M1
(2020)
v8.2 M6
(2020)/cancelled
v8.2 M3 (2018) Exynos 9810)
v8.2 M4 (2019) Exynos 9820)
v8.2 M5 (2019) Exynos 990)
Widening of mobile CPU cores during their evolution -2
v9.0 HP Cortex-X3
(2022)

## Slide 257: 6. Evolution of mobile processors (31)
ARM’s astonishingly dynamic widening their cores in a couple of years [61]
(2018)
(2019)
(2020)
(2022)
As seen, ARM increased the width of their Cortex cores by 50 % within three years.

## Slide 258: 6. Evolution of mobile processors (32)
Widening of mobile CPU cores during their evolution -3
As the above Figures demonstrate, in the last couple of years both ARM, Apple, and Samsung
dramatically widened their mobile cores, as long as early mobile processors were only
1-3 wide, their recent successors provide already 6 to 8-wide cores.
In fact, such core widths were inconceivable a few years earlier yet.

## Slide 259
7. References
Notes: 259

## Slide 260: 7. References (1)
[5]: Fisher S., “Technical Overview of the 45 nm Next Generation Intel Core Microarchitecture
(Penryn),” IDF 2007, ITPS001, http://isdlibrary.intel-dispatch.com/isd/89/45nm.pdf
[6]: Server duel: Xeon Woodcrest vs. Opteron Socket F, Tweakers, Sept. 7 2006,
https://tweakers.net/reviews/646/2/server-duel-xeon-woodcrest-vs-opteron-socket-f-
post-mortem-netburst.html
[7]: Razin A., Core, Nehalem, Gesher. Intel: New Architecture Every Two Years,
Xbit Laboratories, April 28 2006,
http://www.xbitlabs.com/news/cpu/display/20060428162855.html
[1]: Exynos 8 Octa (8890), Samsung, 2016,
http://www.samsung.com/semiconductor/minisite/Exynos/w/solution/mod_ap/8890
[2]: Shilow A., Intel’s Path to 10nm: Past, Present, and Future, EET Asia, June 17, 2020,
https://www.eetasia.com/intels-path-to-10nm-past-present-and-future
[3]: 10_nm lithography process,
https://en.wikichip.org/wiki/10_nm_lithography_process
[4]: Intel eases up in race to 10GHz, The Register, Sept. 25 2002,
https://www.theregister.co.uk/2002/09/25/intel_eases_up_in_race/
[8]: Intel's (INTC) CEO Brian Krzanich on Q2 2015 Results - Earnings Call Transcript, Seeking
Alpha, July 15 2015, http://seekingalpha.com/article/3329035-intels-intc-ceo-brian-
krzanich-on-q2-2015-results-earnings-call-transcript?page=2
[9]: ARS Staff; Intel retires “tick-tock” development model, extending the life of each process; https://arstechnica.com/; 03.23.2016; https://arstechnica.com/information-technology/2016/03/intel-retires-tick-tock-development-model-extending-the-life-of-each-process/

## Slide 261: 7. References (2)
[10]: Cutres I.; Intel’s 10nm Cannon Lake and Core i3-8121U Deep Dive Review; anandtech.com; 25. January 2019.; https://www.anandtech.com/show/13405/intel-10nm-cannon-lake-and-core-i3-8121u-deep-dive-review
[11]: Passingham M., Intel 8th-gen CPUs Revealed: Double the cores, but where’s Coffee Lake?,
Trusted Reviews, Aug. 23 2017, http://www.trustedreviews.com/news/intel-8th-gen-
core-specs-technology-explained-2952599
[12]: Cutress I., Intel’s Manufacturing Roadmap from 2019 to 2029: Back Porting, 7nm, 5nm,
3nm, 2nm, and 1.4 nm, AnandTech, Dec. 11, 2019,
https://www.anandtech.com/show/15217/intels-manufacturing-roadmap-from-2019-to-2029
[13]: Papermaster M., Back in High Performance...To Stay, AMD 2017 Financial Analyst Day,
May 16 2017, http://ir.amd.com/phoenix.zhtml?c=74093&p=irol-analystday
[14]: Vireko K., A Simple Guide To Intel CPU/Processor Naming Scheme (Explained), Tech Consumer Guide, Mai 16, 2019, https://www.techconsumerguide.com/guide-to-intel-cpu-naming
[15]: New Xeon Processor Numbering, More Than Just a Number, Intel.com, April 5 2011,
https://communities.intel.com/community/itpeernetwork/datastack/blog/2011/04/05/
new-xeon-processor-numbering-more-than-just-a-number
[16]: Intel Core 2 Duo Processor E8000 and E7000 Series Datasheet, Intel, Jan. 2009
[17]: Morgan t. P. Deep dive into Intel’s “Ice Lake” Xeon SP architecture, The next platform, April 19, 2021,https://www.nextplatform.com/2021/04/19/deep-dive-into-intels-ice-lake-xeon-sp-architecture/
[18]: Bohr M., Leading at the edge, Technology and manufacturing Day, Intel, 28/03/2017,
https://newsroom.intel.com/newsroom/wp-content/uploads/sites/11/2017/03/
Mark-Bohr-2017-Moores-Law.pdf

## Slide 262: 7. References (3)
[19]: Intel 5th Generation Broadwell Processors Arrive, Cherry Trail Shipping; CdrInfo.com; 5. January 2015.; https://www.cdrinfo.com/sections/news/Print.aspx?NewsId=42515
[20]: Wikipedia, Intel HD and Iris Graphics,
https://en.wikipedia.org/wiki/Intel_HD_and_Iris_Graphics
[21]: oneAPI GPU Optimization Guide; Developer Guide; Intel.com; 11. April 2021.; https://www.intel.com/content/www/us/en/develop/documentation/oneapi-gpu-optimization-guide/top/gen-arch.html
[22]: Cutress I., Hot Chips 2020 Live Blog: Intel's Xe GPU Architecture (5:30pm PT), AnandTech,
Aug. 17 2020, https://www.anandtech.com/show/15993/hot-chips-2020-live-blog-intels-
xe-gpu-architecture-530pm-pt
[23]: Simth R.; The Intel XE-LP GPU Architecture Deep Dive; anadtech.com; 13. August 2020.; https://www.anandtech.com/show/15973/the-intel-xelp-gpu-architecture-deep-dive-building-up-from-the-bottom
[24]: Blythe D., Technology Insight: Next Generation Intel Processor Graphics Architecture
Code Name Skylake, SPCS003, IDF15, San Francisco, Aug. 2015
[25]: X299 XPOWER GAMING AC, MSI,
https://www.msi.com/Motherboard/X299-XPOWER-GAMING-AC.html#productSpecification
-section
[26]: Ung G. M., Intel Broadwell-E Core i7-6950X Review: The first 10-core enthusiast CPU is a
beast, PC World, May 30 2016, http://www.pcworld.com/article/3075433/computers/
intel-broadwell-e-core-i7-6950x-review-the-first-10-core-enthusiast-cpu-is-a-monster.html
[27]: A New Day for the Datacenter, Presentation at AMD Financial Analyst Day, May 16 2017,
http://ir.amd.com/phoenix.zhtml?c=74093&p=irol-analystday

## Slide 263: 7. References (4)
[28]: Coffee Lake - Microarchitectures – Intel, WikiChip (visited on 27 Aug., 2019),
https://en.wikichip.org/wiki/intel/microarchitectures/coffee_lake
[29]: Scansen D., Intel Launches Next Generation of Microprocessors, Engineering, June 10 2013,
http://www.engineering.com/ElectronicsDesign/ElectronicsDesignArticles/ArticleID/
5838/Intel-Launches-Next-Generation-of-Microprocessors.aspx
[30]: Wechsler O., “Inside Intel Core Microarchitecture,” White Paper, Intel, 2006
[31]: Bryant D., “Intel Hitting on All Cylinders,” UBS Conf., Nov. 2007,
http://files.shareholder.com/downloads/INTC/0x0x191011/e2b3bcc5-0a37-4d06-
aa5a-0c46e8a1a76d/UBSConfNov2007Bryant.pdf
[32]: Fisher S., “Technical Overview of the 45nm Next Generation Intel Core Microarchitecture
(Penryn),” IPTS001, Fall IDF 2007, http://isdlibrary.intel-dispatch.com/isd/89/45nm.pdf
[33]: Cutress I., The Intel Skylake Mobile and Desktop Launch, with Architecture Analysis,
AnandTech, Sept. 1 2015, http://www.anandtech.com/show/9582/intel-skylake-mobile-
desktop-launch-architecture-analysis
[34]: Eul H., Bell M., Mobile at Intel, Investor Meeting 2012,
http://www.cnx-software.com/pdf/Intel_2012/2012_Intel_Investor_Meeting_Eul_Bell.pdf
[35]: Lee V., “Inside the Intel Core Microarchitecture,” IDF, May 2006, Shenzhen,
http://www.prcidf.com.cn/sz/systems_conf/track_sz/SMC/Intel%20Core%20uArch.pdf
[36]: Qualcomm dominates smartphone chip and baseband, tablet processor markets, Mobile
Europe, February 17 2014
http://www.mobileeurope.co.uk/Press-Wire/qualcomm-dominates-smartphone-chip-and
-baseband-tablet-processor-markets

## Slide 264: 7. References (5)
[37]: Völkel F., “Duel of the Titans: Opteron vs. Xeon : Hammer Time: AMD On The Attack,”
Tom’s Hardware, Apr. 22 2003,
http://www.tomshardware.com/reviews/duel-titans,620.html
[38]: George V., Piazza T., Jiang H.: Technology Insight: Intel Next Generation Microarchitecture
Codename Ivy Bridge, IDF 2011
[39]: Smith R., Intel's Changing Future: Smartphone SoCs Broxton & SoFIA Officially Cancelled,
AnandTech, April 29, 2016,
http://www.anandtech.com/show/10288/intel-broxton-sofia-smartphone-socs-cancelled
[40]: Intel Timna Microprocessor Family, CPU World, http://www.cpu-world.com/CPUs/Timna/
[41]: Olivera, A régóta várt Intel Ivy Bridge tesztje, Prohardware, April 13 2012,
http://prohardver.hu/teszt/intel_ivy_bridge_teszt/az_ivy_bridge.html
[42]: Shimpi a. L. & Smith R., The Intel Ivy Bridge (Core i7 3770K) Review, AnandTech, April 23, 2012,
https://www.anandtech.com/show/5771/the-intel-ivy-bridge-core-i7-3770k-review/4
[43]: Wright A., Intel 12th Gen Alder Lake vs. AMD Ryzen 5000: Which Should You Get?, MUO,
17. Jan., 2021,
https://www.makeuseof.com/intel-12th-gen-vs-amd-ryzen-5000/
[44]: Crider M., Intel 12th-gen ‘Alder Lake’ vs. Ryzen 5000: 5 key things to know, PCWorld, 04. Nov. 2021,
https://www.pcworld.com/article/549847/intel-alder-lake-vs-ryzen-5000-5-things-to-know.html
[45]: Smith R., AMD Details Ryzen 7000 Launch: Ryzen 7950X and More, Coming sept. 27th,
https://www.anandtech.com/show/17552/amd-details-ryzen-7000-launch-up-ryzen-7950x-
coming-sept-27

## Slide 265: 7. References (6)
[46]: Cutress I., AMD Ryzen 5000 and Zen 3 on Nov 5th: +19% IPC, Claims Best Gaming CPU,
AnandTech, Oct. 8, 2020,
https://www.anandtech.com/print/16148/amd-ryzen-5000-and-zen-3-on-nov-5th-19-
ipc-claims-best-gaming-CPU
[47]: Hwang c., TSMC dossier (4): Technology contention among world-class leaders, Digitimes,
17. July, 2021, https://www.digitimes.com/news/a20210713VL201.html
[48]: Cutress I., The Snapdragon 8 Gen 1 Performance Preview: Sizing Up Cortex-X2, AnandTech, Dec. 14, 2021, https://www.anandtech.com/show/17102/snapdragon-8-gen-1-performance-preview-sizing-up-cortex-x2/2
[49]: Frumusanu A., Arm Announces Neoverse V1, N2 Platforms & CPUs, CMN-700 Mesh: More
Performance, More Cores, More Flexibility, anandTech, April 27, 2021,
https://www.anandtech.com/print/16640/arm-announces-neoverse-v1-n2-platforms-
cpus-cmn700-mesh
[50]: Holt W., Advancing Moore's Law: Benefits Across the Portfolio, Investor Meeting, Nov. 21
2013,http://www.semiwiki.com/forum/files/Intel%20Manufacturing%20Slides%202013.pdf
[51]: Jones S., Intel Node Names, IC Knowledge, Intel, Semiconductor Services; https://semiwiki.com/; February 15, 2021,
https://semiwiki.com/semiconductor-manufacturers/intel/295767-intel-nodes/
[52]: Leibson SIntel Welcomes You to the Angstrom Era PS: Moore’s Law is Still Dead; https://www.eejournal.com/; November 01, 2021,
https://www.eejournal.com/article/intel-welcomes-you-to-the-angstrom-era/

## Slide 266: 7. References (7)
[54]: Lal Shimpi A., Intel Core 2 Extreme QX6850 and Massive Price Cuts,
AnandTech, July 16, 2007,
https://www.anandtech.com/show/2276/6
[53]: Völkel F., “Duel of the Titans: Opteron vs. Xeon : Hammer Time: AMD On The Attack,”
Tom’s Hardware, Apr. 22 2003,
http://www.tomshardware.com/reviews/duel-titans,620.html
[55]: Connatser M., AMD Ryzen 7000 vs. Intel Raptor Lake; https://www.digitaltrends.com/,
Oct. 20, 2022,
https://www.digitaltrends.com/computing/amd-ryzen-7000-vs-intel-raptor-lake/
[56]: George W., What Happened to High End Desktop (HEDT) Processors?;
https://www.pugetsystems.com/; May 09. 2022;
https://www.pugetsystems.com/blog/2022/05/09/what-happened-to-high-end- desktop-hedt-processors-2329/
[57]: btarunr., Intel "Sapphire Rapids" Xeon 4-tile MCM Annotated; https://www.techpowerup.com/,
Febr. 21, 2022,
https://www.techpowerup.com/292204/intel-sapphire-rapids-xeon-4-tile-mcm-annotated
[58]: Hamblen M., Intel CEO Gelsinger at Hot Chips focuses on chiplets for speed; https://www.fierceelectronics.com/; Aug. 22, 2022; https://www.fierceelectronics.com/sensors/intel-features-meteor-lake-hot-chips-focus-chiplets-speed
[59]: Pirzada U., Ivy Bridge-EX Arrives – Intel Xeon E7 v2 Released with 20 New SKU Lineup; https://wccftech.com/; Febr. 19, 2014; https://wccftech.com/ivy-bridge-ex-arrives-intel-xeon-e7-v2-released/

## Slide 267: 7. References (8)
[61]: Schor D., Arm Unveils Next-Gen Flagship Core: Cortex-X3, use.wikichip.org, Jun. 28, 2022,
https://fuse.wikichip.org/news/6855/arm-unveils-next-gen-flagship-core-cortex-x3/
[60]: Dr. Cutress I., Intel Xeon Sapphire Rapids: How To Go Monolithic with Tiles,
AnandTech, Aug. 31, 2021,
https://www.anandtech.com/show/16921/intel-sapphire-rapids-nextgen-xeon-scalable-gets-a-tiling-upgrade/2
[62]: Bonshor G, Intel Core i9-l3900K and i5-l3600K Review: Raptor Lake Brings More Bite, AnandTech, Oct. 20, 2022,
https://www.anandtech.com/print/17601/intel-core-i9-13900k-and-i5-13600k-review
[63]: Bonshor G., Intel To Launch New Core Processor Branding for Meteor Lake: Drop the i,
Add Ultra Tier, AnandTech, June 15, 2023,
https://www.anandtech.com/show/18911/intel-new-core-branding-for-meteor-lake-no
-i-new-ultra-tier