## Slide 1
Dezső Sima
Intel’s Core2 family – The TOCK lines I
Introduction and the Core 2 line
August 2018
Vers. 3.0

## Slide 2
Contents
1. Introduction
2. The Core 2 line
3. The Nehalem line
4. The Sandy Bridge line
5. The Haswell line
6. The Skylake line
7. The Kaby Lake line
8. The Kaby Lake Refresh line
9. The Coffee Lake line
10. The Cannon Lake line (outlook)

## Slide 3
1. Introduction
1.1 Overview of the evolution of Intel's Pentium 4 and
Core 2 families
1.2 Evolution of desktop and laptop processors
1.3 Evolution of HEDs (High-End desktops)
1.4 Evolution of high-end 4S/8S servers
1.5 Evolution of tablet and smartphone processors
Notes: 3

## Slide 4
1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families
Notes: 4

## Slide 5: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (1)
Key new features of the ISP
and the microarchitecture
New microarch., 64-bit
Dual cores (DC) for the
Pentium D (Smithfield) (05/2005)
01/2006
90nm
130nm
TICK TOCK
2 YEARS
2 YEARS
2 YEARS
65nm
TICK Pentium 4 (Cedar Mill SC)
Pentium D (Presler DC)
TOCK Core 2
2 YEARS
New microarch.
called Netburst
New microarch.,
Hyperthreading (HT)
Pentium 4 /Northwood
TICK TOCK
TICK TOCK
Pentium 4 /Prescott
Pentium 4 /Willamette
07/2006
11/2000
01/2002
02/2004
180nm
*
Note
This is a single phase development model, in each generation both technology and
microarchitecture is changed.
1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (Based on [3])
The Core 2 family was preceded by the Pentium 4 family
The Pentim 4 family introduced important innovations, but gave rise to far reaching implications,
as detailed next.

## Slide 6: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (2)
At Pentium 4's launch (Nov. 2000) Intel's vice president (Otellini) claimed the lifespan of the
Netburst microarchitecture to be 7 years and expected its clock frequency to break the
10 GHz mark in 2006 [219].
Design target of the Pentium 4 family

## Slide 7: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (3)
Intel's Pentium 4 family
180 nm
130 nm
90 nm

## Slide 8: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (4)
Relative dissipation of Intel's x86 family of processors
Pentium 4
Pentium III
Pentium

## Slide 9: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (5)
Figure: In Oct. 2004 Crag Barrett, Intel's then-CEO on his knees to apologize for not achieving the
4GHz mark in front of an audience of 7000 informatics professional at the IT Expo in Orlando [220]
Intel's cancellation of 4 GHz Pentium 4 devices and subsequently the Pentium 4 line
In Oct. 2004 Intel's CEO (Chief Executing Officer) admitted that the Pentium 4 family
would not achieve 4 GHz [220]. f

## Slide 10
Changing Intel's design paradigm to cope with raising dissipation about 2003
In 2003 Intel shifted the focus of their processor development from the pure performance goal
to the aspect of performance per watt, as stated in a slide from 4/2006, see below.
Figure 1.3: Intel’s plan to develop their manufacturing technology and processor lines
revealed at a shareholder’s meeting back in 4/2006 [74]
1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (6)
*

## Slide 11
High performance/power
(e.g. GFLOPS/Watt)
Traditional processors
Tablets and smartphones
Low power
(Watt)
(Number of operating hours)
With the advent of mobile devices (about 2006) a new design paradigm arose for those devices.
Mobile devices require long operating hours i.e. low power consumption, this is contrast to the
design paradigm of traditional processors, as indicated below.
1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (7)
Remark: A further change of the design paradigm for designing the mobile processors
*

## Slide 12: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (8)
Introducing a two-phase development model (Tick-Tock model)for the Core 2 family
The two-phase model reduces the complexity of the development, as
the Tick phase focuses on the reduction of the feature size whereas
the Tock phase focuses on enhancing the microarchitecture.
*

## Slide 13: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (9)
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
Haifa
Oregon
Oregon
Oregon
Haifa
Haifa
Oregon
Oregon
Haifa
Haifa
Haifa
1.1.2 Overview of the evolution of Intel's Pentium 4 and Core 2 families - The generations
1. Introduction (1)
Skylake
New
Microarch.
14 nm
TOCK
TOCK
6. gen.
TOCK
7. gen.
8. gen.1
Kaby Lake
New
Microarch.
14 nm
Kaby Lake
Refresh
New
Microarch.
14 nm
Ice
Lake?
New
Process
10 nm
TICK
9. gen.
Remark
The Haifa (Israel) Development Center
was also responsible for the 8080 and
Pentium M (Banias, Dothan, Jonah
(Core Solo/Core Duo)) processors
beyond Kaby Lake Refresh also the
Kaby Lake G with AMD Vega graphics
Coffee Lake and
10 nm Cannon Lake designs [218].
1Astonishingly, the 8th generation encompasses

## Slide 14: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (10)
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
(2006)
(2007)
(2008)
(2010)
(2011)
(2012)
(2013)
(2014)
Overview of the evolution of Intel's Pentium 4 and Core 2 families - the generations
1. Introduction (1)
(2015)
(2016)
(2017)
Skylake
New
Microarch.
14 nm
TOCK
TOCK
6. gen.
TOCK
7. gen.
8. gen.1
Kaby Lake
New
Microarch.
14 nm
Kaby Lake
Refresh
New
Microarch.
14 nm
Ice
Lake?
New
Process
10 nm
TICK
9. gen.
(2018)
beyond Kaby Lake Refresh also the
Kaby Lake G with AMD Vega graphics
Coffee Lake and
10 nm Cannon Lake designs [218].
1Astonishingly, the 8th generation encompasses

## Slide 15: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (11)
Basic designations of Intel’s processor lines
1. Introduction (1)
i7-78xx/i9-79xx
v5/SP
v6
Skylake
New
Microarch.
14 nm
TOCK
TOCK
6. gen.
(6xxx)
TOCK
7. gen.
(7xxx)
8. gen.1
(8xxx)
Kaby Lake
New
Microarch.
14 nm
Kaby Lake
Refresh
New
Microarch.
14 nm
Ice Lake?
New
Process
10 nm
TICK
9. gen.
HED
S
EE
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
gen.
4/5/6xxx
2. gen.
2xxx
3. gen.
3xxx
4. gen.
4xxx
5. gen.
5xxx
Broad-
well
New
Process
14 nm
TICK
HED
S
38/39xx
E3/E5/E7-xxxx
48/49xx
v2
58/59xx
v3
68/69xx
v4
i5/i7-xxx
980/990
E7-xxx
i7-965/975
3/5xxx
i3/i5/i7-xxx
M/DT
QX 96/97xx
3/5/7xxx
X/QX 6xxx
3/5/7xxx
6/7/8/9xxx
M/DT
beyond Kaby Lake Refresh also the
Kaby Lake G with AMD Vega graphics
Coffee Lake and
10 nm Cannon Lake designs [218].
1Astonishingly, the 8th generation encompasses

## Slide 16
Basic architectures | Basic architectures and their shrinks
Pentium 4 (Prescott) | 2005 90 nm Pentium 4 2006 65 nm Pentium 4
Core 2 | 2006 65 nm Core 2 2007 45 nm Penryn
Nehalem | 2008 45 nm Nehalem 2010 32 nm Westmere
Sandy Bridge | 2011 32 nm Sandy Bridge 2012 22 nm Ivy Bridge
Haswell | 2013 22 nm Haswell 2014 14 nm Broadwell
Skylake | 2015 14 nm Skylake 14 nm Kaby Lake 14 nm Coffee Lake 10 nm Cannon Lake
Icelake | 2019? 10 nm Icelake
1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (12)
Basic microarchitectures and their related shrinks
Considered from the Pentium 4 Prescott core (the third core of Pentium 4) on.

## Slide 17: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (13)
The last two technology transitions have signaled that our cadence today is closer to 2.5 years than two“ [180].
On Intel’s Q2 2015 earnings conference call, on July 16 2015, Krzanich, Intel's CEO (Chief Executive Officer) told:
in the second half of 2017, we expect to launch our first 10-nanometer product, code named Cannonlake.
Evolution of Intel’s IC technology
2000
2002
2004
2006
2008
2010
2012
2014
2016
2018
200
180
160
140
120
100
80
60
40
0
20
180 nm
130 nm
90 nm
65 nm
45 nm
32 nm
22 nm
14 nm
10 nm
Pentium 4
Northwood
Pentium 4
Prescott
Pentium 4
Cedar Mill
Penryn
Westmere
Ivy Bridge
Broadwell
Pentium 4
Willamette
Cannon lake
01/02
02/04
11/07
01/10
04/12
09/14
11/00
2H/17
01/06
nm
2018
*

## Slide 18: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (14)
Intel’s two-phase development model (Tick-Tock model) used for the Core 2 lines -21
Figure is based on [3])
*
2 YEARS
Key new features of the ISP
and the microarchitecture
New microarch.: 4-wide core,
128-bit SIMD FX/FP EUs,
shared L2 , no HT
11/2007
01/2006
65nm
TICK Pentium 4 ( Cedar Mill)
Pentium D (Presler)
TOCK Core 2
07/2006
11/2008
New microarch.: 256-bit (FP) AVX,
ring bus, integrated GPU
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
New microarch.: 256-bit (FX) AVX2,
L4 cache (discrete eDRAM), TSX
06/2013
09/2014
Shared Virtual Memory
10/2015
New microarch.: 5-wide core,
ISP, Memory Side L4 cache
In package integrated GPU
14nm
4 YEARS
TICK Broadwell
TOCK Skylake
New microarch.: 4 cores, integr. MC,
QPI, private L2, (inclusive) L3, HT
TOCK Coffee Lake
TOCK Kaby Lake
08/2016
10/2017
2 YEARS
10nm
TICK Cannonlake
TOCK Icelake
05/2018
??/2019
?? YEARS
Optane memory, in KBL G series:
in package integr. CPU, GPU, HBM2
AVX512
(USB Gen. 2, integr. conn., Optane 2)

## Slide 19: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (14b)
Intel’s two-phase development model (Tick-Tock model) used for the Core 2 lines -21
Figure is based on [3])
*
2 YEARS
Key new features of the ISP
and the microarchitecture
New microarch.: 4-wide core,
11/2007
01/2006
65nm
TICK Pentium 4 ( Cedar Mill)
Pentium D (Presler)
TOCK Core 2
07/2006
11/2008
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
06/2013
09/2014
10/2015
New microarch.: 5-wide core,
14nm
4 YEARS
TICK Broadwell
TOCK Skylake
TOCK Coffee Lake
TOCK Kaby Lake
08/2016
10/2017
2 YEARS
10nm
TICK Cannonlake
TOCK Icelake
05/2018
??/2019
?? YEARS

## Slide 20: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (14c)
Intel’s two-phase development model (Tick-Tock model) used for the Core 2 lines -21
Figure is based on [3])
*
2 YEARS
Key new features of the ISP
and the microarchitecture
128-bit SIMD FX/FP EUs,
11/2007
01/2006
65nm
TICK Pentium 4 ( Cedar Mill)
Pentium D (Presler)
TOCK Core 2
07/2006
11/2008
New microarch.: 256-bit (FP) AVX,
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
New microarch.: 256-bit (FX) AVX2,
06/2013
09/2014
10/2015
14nm
4 YEARS
TICK Broadwell
TOCK Skylake
TOCK Coffee Lake
TOCK Kaby Lake
08/2016
10/2017
2 YEARS
10nm
TICK Cannonlake
TOCK Icelake
05/2018
??/2019
?? YEARS
AVX512

## Slide 21: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (14d)
Intel’s two-phase development model (Tick-Tock model) used for the Core 2 lines -21
Figure is based on [3])
*
2 YEARS
Key new features of the ISP
and the microarchitecture
shared L2
11/2007
01/2006
65nm
TICK Pentium 4 ( Cedar Mill)
Pentium D (Presler)
TOCK Core 2
07/2006
11/2008
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
L4 cache (discrete eDRAM)
06/2013
09/2014
10/2015
Memory Side L4 cache
14nm
4 YEARS
TICK Broadwell
TOCK Skylake
, private L2, (inclusive) L3
TOCK Coffee Lake
TOCK Kaby Lake
08/2016
10/2017
2 YEARS
10nm
TICK Cannonlake
TOCK Icelake
05/2018
??/2019
?? YEARS

## Slide 22: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (14e)
Intel’s two-phase development model (Tick-Tock model) used for the Core 2 lines -21
Figure is based on [3])
*
2 YEARS
Key new features of the ISP
and the microarchitecture
no HT
11/2007
01/2006
65nm
TICK Pentium 4 ( Cedar Mill)
Pentium D (Presler)
TOCK Core 2
07/2006
11/2008
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
06/2013
09/2014
10/2015
14nm
4 YEARS
TICK Broadwell
TOCK Skylake
HT
TOCK Coffee Lake
TOCK Kaby Lake
08/2016
10/2017
2 YEARS
10nm
TICK Cannonlake
TOCK Icelake
05/2018
??/2019
?? YEARS

## Slide 23: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (14f)
Intel’s two-phase development model (Tick-Tock model) used for the Core 2 lines -21
Figure is based on [3])
*
2 YEARS
Key new features of the ISP
and the microarchitecture
11/2007
01/2006
65nm
TICK Pentium 4 ( Cedar Mill)
Pentium D (Presler)
TOCK Core 2
07/2006
11/2008
integrated GPU
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
06/2013
09/2014
10/2015
ISP
14nm
4 YEARS
TICK Broadwell
TOCK Skylake
TOCK Coffee Lake
TOCK Kaby Lake
08/2016
10/2017
2 YEARS
10nm
TICK Cannonlake
TOCK Icelake
05/2018
??/2019
?? YEARS

## Slide 24: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (15)
2 YEARS
Key new features
in power management
11/2007
01/2006
65nm
TICK Pentium 4 ( Cedar Mill)
Pentium D (Presler)
TOCK Core 2
07/2006
11/2008
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
06/2013
09/2014
10/2015
14nm
4 YEARS
TICK Broadwell
TOCK Skylake
TOCK Coffee Lake
TOCK Kaby Lake
08/2016
10/2017
2 YEARS
10nm
TICK Cannonlake
TOCK Icelake
05/2018
??/2019
Clock gating, PECI,
Platform Thermal Control by
3. party controller
EDAT
Integrated Power Gates, PCU,
Turbo Boost
Turbo Boost 2.0
FIVR
2. gen. FIVR
Speed Shift Technology,
Duty Cycle control, No FIVR
(except Skylake X)
Speed Shift Technology v2
Intel’s two-phase development model (Tick-Tock model) used for the Core 2 lines -2
*
In H-series: TVB
(Thermal Velocity Boost)
Figure is based on [3])

## Slide 25: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (15b)
2 YEARS
Key new features
in power management
11/2007
01/2006
65nm
TICK Pentium 4 ( Cedar Mill)
Pentium D (Presler)
TOCK Core 2
07/2006
11/2008
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
06/2013
09/2014
10/2015
14nm
4 YEARS
TICK Broadwell
TOCK Skylake
TOCK Coffee Lake
TOCK Kaby Lake
08/2016
10/2017
2 YEARS
10nm
TICK Cannonlake
TOCK Icelake
05/2018
??/2019
Clock gating
Integrated Power Gates
Intel’s two-phase development model (Tick-Tock model) used for the Core 2 lines -2
*
Figure is based on [3])

## Slide 26: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (15c)
2 YEARS
Key new features
in power management
11/2007
01/2006
65nm
TICK Pentium 4 ( Cedar Mill)
Pentium D (Presler)
TOCK Core 2
07/2006
11/2008
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
06/2013
09/2014
10/2015
14nm
4 YEARS
TICK Broadwell
TOCK Skylake
TOCK Coffee Lake
TOCK Kaby Lake
08/2016
10/2017
2 YEARS
10nm
TICK Cannonlake
TOCK Icelake
05/2018
??/2019
PECI,
Platform Thermal Control by
3. party controller
PCU
Speed Shift Technology,
Duty Cycle control,
Speed Shift Technology v2
Intel’s two-phase development model (Tick-Tock model) used for the Core 2 lines -2
*
Figure is based on [3])

## Slide 27: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (15d)
2 YEARS
Key new features
in power management
11/2007
01/2006
65nm
TICK Pentium 4 ( Cedar Mill)
Pentium D (Presler)
TOCK Core 2
07/2006
11/2008
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
06/2013
09/2014
10/2015
14nm
4 YEARS
TICK Broadwell
TOCK Skylake
TOCK Coffee Lake
TOCK Kaby Lake
08/2016
10/2017
2 YEARS
10nm
TICK Cannonlake
TOCK Icelake
05/2018
??/2019
EDAT
Turbo Boost
Turbo Boost 2.0
Intel’s two-phase development model (Tick-Tock model) used for the Core 2 lines -2
*
Figure is based on [3])

## Slide 28: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (15e)
2 YEARS
Key new features
in power management
11/2007
01/2006
65nm
TICK Pentium 4 ( Cedar Mill)
Pentium D (Presler)
TOCK Core 2
07/2006
11/2008
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
06/2013
09/2014
10/2015
14nm
4 YEARS
TICK Broadwell
TOCK Skylake
TOCK Coffee Lake
TOCK Kaby Lake
08/2016
10/2017
2 YEARS
10nm
TICK Cannonlake
TOCK Icelake
05/2018
??/2019
FIVR
2. gen. FIVR
No FIVR
(except Skylake X)
Intel’s two-phase development model (Tick-Tock model) used for the Core 2 lines -2
*
Figure is based on [3])

## Slide 29: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (16)
Per Generation
Cumulative
Pentium M Dothan
Core 2
Penryn
NHM (w/o SMT)
WSM
SNB
IVB
HSW
BRW
1.8
1.7
1.6
1.5
1.4
1.3
1.1
1.2
1
2
1.9
20%
18%
16%
14%
12%
10%
8%
6%
4%
2%
0%
24%
22%
SKL
Raising of the single thread IPC in Intel’s basic architectures (Based on [195])
Note that Intel raised IPC in the Core family only less then 2-times in about 10 years.
Tock models contribute by about 10 %, Tick models by about 5 % for raising IPC.
*

## Slide 30: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (17)
Presentation at AMD's Financial Analyst Day May 16 2017
General implications of the evolution of transistor technology [245]
*

## Slide 31: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (18)
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smarphones
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smartphones
Desktops
Smarphones
Servers
Recent processor categories of Intel
Smartphones
Tablets
Atom lines
Xeon E7/E5/E3
Platinum/Gold etc.
Desktops/Laptops
(Client computing)
Core i7/i5/i3
(Basic architectures)
Atom lines
(+ LP Core models)
HEDs
(High-End Desktops)
Core i7/i9
(Extreme Edition
or X models)
*
Up to 28C
2C - 18C
(Up to 4C - 10C + G)
(by other vendors)
2C - 6C + G
C a n c e l l e d i n 2 0 1 6
Typical config.

## Slide 32: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (19)
14 nm dies of Intel's different processor categories (not on scale) [247]
Knights Landing (72C, ~680 mm2)
Skylake-SP (28C, ~680 mm2)
Skylake (4C, 122 mm2)
Broadwell (2C, 82 mm2)

## Slide 33: 1.1 Overview of the evolution of Intel's Pentium 4 and Core 2 families (19)
14 nm dies of Intel's different processor categories (approximately on scale)
[247]
Broadwell (2C, 82 mm2)
Skylake (4C, 122 mm2)
Skylake-SP (28C, ~680 mm2)

## Slide 34
1.2 Evolution of desktop and laptop processors
Notes: 34

## Slide 35: 1.2 Evolution of desktop and laptop processors (1)
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smarphones
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smartphones
Desktops
Smarphones
Servers
Recent processor categories of Intel
Smartphones
Tablets
Atom lines
Xeon E7/E5/E3
Platinum/Gold etc.
Desktops/Laptops
(Client computing)
Core i7/i5/i3
(Basic architectures)
Atom lines
(+ LP Core models)
HEDs
(High-End Desktops)
Core i7/i9
(Extreme Edition
or X models)
1.2 Evolution of desktop and laptop processors

## Slide 36
Designation of the platform | Platform topology | Processor | Technology | Max. no. of cores (nC) | Year of introduction | Processor socket | MCH/PCH | Highest mem./ speed | No. of mem. channels
Anchor Creek | Off-die MC | Pentium D | 90 nm | 2x1 | 5/2005 | LGA 775 | 945-955 | DD2-667 | 2
Bridge Creek |  | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
Salt Creek |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series (Bearlake) | DDR3-1067 | 2
Boulder Creek |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series (Eaglelake) | DDR3-1067 | 2
Kings Creek | On-die MC | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series (Ibex Peak) | DDR3-1333 | 2
 |  | Westmere (Clarkdale) | 32 nm | 2C+G | 1/2010 | LGA 1156 | 5 Series (Ibex Peak) |  | 
 |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | LGA 1155 | 6 series (Cougar Point) | DDR3-1333 | 2
Sugar Bay |  |  |  |  |  |  |  |  | 
Maho Bay |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 | LGA 1155 | 7 series (Panther Point) | DDR3-1600 | 2
Shark Bay |  | Haswell | 22 nm | 4C+G | 6/2013 | LGA 1155 | 8 Series (Lynx Point) | DDR3-1600 | 2
 |  | Haswell refresh | 22 nm | 4C+G | 5/2014 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1666 | 
 |  | Broadwell | 14 nm | 4C+G | 6/2015 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1866 | 
 |  | Skylake | 14 nm | 4C+G | 10/2015 | LGA 1151 | Series (Sunrise Point) | DDR4-2133 | 2
 |  | Kaby Lake | 14 nm | 4C + G | 8/2016 | LGA 1151 | 200 Series | DDR4-2400 | 2
 |  | Coffee Lake | 14 nm | 6C+G | 10/2017 | LGA 1151 | 300 Series | DDR4-2666 | 2
Intel’s Core-based mainstream DT platforms
1.2 Evolution of desktop and laptop processors (2)

## Slide 37
Designation of the platform | Platform topology | Processor | Technology | Max. no. of cores (nC) | Year of introduction | Processor socket | MCH/PCH | Highest mem./ speed | No. of mem. channels
Anchor Creek | Off-die MC | Pentium D | 90 nm | 2x1 | 5/2005 | LGA 775 | 945-955 | DD2-667 | 2
Bridge Creek |  | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
Salt Creek |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series (Bearlake) | DDR3-1067 | 2
Boulder Creek |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series (Eaglelake) | DDR3-1067 | 2
Kings Creek | On-die MC | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series (Ibex Peak) | DDR3-1333 | 2
 |  | Westmere (Clarkdale) | 32 nm | 2C+G | 1/2010 | LGA 1156 | 5 Series (Ibex Peak) |  | 
 |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | LGA 1155 | 6 series (Cougar Point) | DDR3-1333 | 2
Sugar Bay |  |  |  |  |  |  |  |  | 
Maho Bay |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 | LGA 1155 | 7 series (Panther Point) | DDR3-1600 | 2
Shark Bay |  | Haswell | 22 nm | 4C+G | 6/2013 | LGA 1155 | 8 Series (Lynx Point) | DDR3-1600 | 2
 |  | Haswell refresh | 22 nm | 4C+G | 5/2014 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1666 | 
 |  | Broadwell | 14 nm | 4C+G | 6/2015 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1866 | 
 |  | Skylake | 14 nm | 4C+G | 10/2015 | LGA 1151 | Series (Sunrise Point) | DDR4-2133 | 2
 |  | Kaby Lake | 14 nm | 4C + G | 8/2016 | LGA 1151 | 200 Series | DDR4-2400 | 2
 |  | Coffee Lake | 14 nm | 6C +G | 10/2017 | LGA 1151 | 300 Series | DDR4-2666 | 2
Max. number of cores
1.2 Evolution of desktop and laptop processors (3)

## Slide 38
Designation of the platform | Platform topology | Processor | Technology | Max. no. of cores (nC) | Year of introduction | Processor socket | MCH/PCH | Highest mem./ speed | No. of mem. channels
Anchor Creek | Off-die MC | Pentium D | 90 nm | 2x1 | 5/2005 | LGA 775 | 945-955 | DD2-667 | 2
Bridge Creek |  | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
Salt Creek |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series (Bearlake) | DDR3-1067 | 2
Boulder Creek |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series (Eaglelake) | DDR3-1067 | 2
Kings Creek | On-die MC | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series (Ibex Peak) | DDR3-1333 | 2
 |  | Westmere (Clarkdale) | 32 nm | 2C+G | 1/2010 | LGA 1156 | 5 Series (Ibex Peak) |  | 
 |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | LGA 1155 | 6 series (Cougar Point) | DDR3-1333 | 2
Sugar Bay |  |  |  |  |  |  |  |  | 
Maho Bay |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 | LGA 1155 | 7 series (Panther Point) | DDR3-1600 | 2
Shark Bay |  | Haswell | 22 nm | 4C+G | 6/2013 | LGA 1155 | 8 Series (Lynx Point) | DDR3-1600 | 2
 |  | Haswell refresh | 22 nm | 4C+G | 5/2014 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1666 | 
 |  | Broadwell | 14 nm | 4C+G | 6/2015 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1866 | 
 |  | Skylake | 14 nm | 4C+G | 10/2015 | LGA 1151 | Series (Sunrise Point) | DDR4-2133 | 2
 |  | Kaby Lake | 14 nm | 4C + G | 8/2016 | LGA 1151 r1 | 200 Series (Union Point) | DDR4-2400 | 2
 |  | Coffee Lake | 14 nm | 6C +G | 10/2017 | LGA 1151 r2 | 300 Series | DDR4-2666 | 2
Number of memory channels
1.2 Evolution of desktop and laptop processors (4)

## Slide 39
Designation of the platform | Platform topology | Processor | Technology | Max. no. of cores (nC) | Year of introduction | Processor socket | MCH/PCH | Highest mem./ speed | No. of mem. channels
Anchor Creek | Off-die MC | Pentium D | 90 nm | 2x1 | 5/2005 | LGA 775 | 945-955 | DD2-667 | 2
Bridge Creek |  | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
Salt Creek |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series (Bearlake) | DDR3-1067 | 2
Boulder Creek |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series (Eaglelake) | DDR3-1067 | 2
Kings Creek | On-die MC | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series (Ibex Peak) | DDR3-1333 | 2
 |  | Westmere (Clarkdale) | 32 nm | 2C+G | 1/2010 | LGA 1156 | 5 Series (Ibex Peak) |  | 
 |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | LGA 1155 | 6 series (Cougar Point) | DDR3-1333 | 2
Sugar Bay |  |  |  |  |  |  |  |  | 
Maho Bay |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 | LGA 1155 | 7 series (Panther Point) | DDR3-1600 | 2
Shark Bay |  | Haswell | 22 nm | 4C+G | 6/2013 | LGA 1155 | 8 Series (Lynx Point) | DDR3-1600 | 2
 |  | Haswell refresh | 22 nm | 4C+G | 5/2014 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1666 | 
 |  | Broadwell | 14 nm | 4C+G | 6/2015 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1866 | 
 |  | Skylake | 14 nm | 4C+G | 10/2015 | LGA 1151 | Series (Sunrise Point) | DDR4-2133 | 2
 |  | Kaby Lake | 14 nm | 4C + G | 8/2016 | LGA 1151 | 200 Series | DDR4-2400 | 2
 |  | Coffee Lake | 14 nm | 6C +G | 10/2017 | LGA 1151 | 300 Series | DDR4-2666 | 2
Platform topology
1.2 Evolution of desktop and laptop processors (5)

## Slide 40: 1.2 Evolution of desktop and laptop processors (6)
SMPs
(Symmetrical MultiProcessor)
Basic platform topologies of multiprocessors
classified according to their memory architecture
NUMAs
Multiprocessors (Multi socket system)
with Non-Uniform Memory Access
Multiprocessors (Multi socket system)
with Uniform Memory Access (UMA)
Typical examples
Processor
MCH
ICH
FSB
Processor
E.g. DDR2-533
ESI
E.g. DDR3-1333
Processor
IOH1
QPI
QPI
ICH
ESI
QPI
E.g. DDR3-1333
Processor
All processors access main memory by the same
mechanism, (e.g. by individual FSBs and an MCH).
A particular part of the main memory can be accessed
by each processor immediately, other parts remotely.
1ICH: I/O hub
ESI: Enterprise System Interface
Changing the basic platform topology of MP platforms from SMP to NUMA -2
*

## Slide 41
Designation of the platform | Platform topology | Processor | Technology | Max. no. of cores (nC) | Year of introduction | Processor socket | MCH/PCH | Highest mem./ speed | No. of mem. channels
Anchor Creek | Off-die MC (SMP) | Pentium D | 90 nm | 2x1 | 5/2005 | LGA 775 | 945-955 | DD2-667 | 2
Bridge Creek |  | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
Salt Creek |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series (Bearlake) | DDR3-1067 | 2
Boulder Creek |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series (Eaglelake) | DDR3-1067 | 2
Kings Creek | On-die MC (NUMA) | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series (Ibex Peak) | DDR3-1333 | 2
 |  | Westmere (Clarkdale) | 32 nm | 2C+G | 1/2010 | LGA 1156 | 5 Series (Ibex Peak) |  | 
 |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | LGA 1155 | 6 series (Cougar Point) | DDR3-1333 | 2
Sugar Bay |  |  |  |  |  |  |  |  | 
 |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 | LGA 1155 | 7 series (Panther Point) | DDR3-1600 | 2
 |  | Haswell | 22 nm | 4C+G | 6/2013 | LGA 1155 | 8 Series (Lynx Point) | DDR3-1600 | 2
 |  | Haswell refresh | 22 nm | 4C+G | 5/2014 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1666 | 
 |  | Broadwell | 14 nm | 4C+G | 6/2015 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1866 | 
 |  | Skylake | 14 nm | 4C+G | 10/2015 | LGA 1151 | Series (Sunrise Point) | DDR4-2133 | 2
 |  | Kaby Lake | 14 nm | 4C + G | 8/2016 | LGA 1151 | 200 Series | DDR4-2400 | 2
 |  | Coffee Lake | 14 nm | 6C? +G | 10/2017 | LGA 1151 | 300 Series | DDR4-2666 ? | 2
Speeding up the memory rate
1.2 Evolution of desktop and laptop processors (7)

## Slide 42: 1.2 Evolution of desktop and laptop processors (8)
Key features of the evolution of Intel’s Core-based mainstream DT platforms
Their core count rose soon (already in 2007) to 4 and remain at this figure.
Two memory channels are used to connect memory.
Memory is connected up to the Penryn via the MCH thereafter immediately via the processor.
In a 10 year period memory speed rose about three to four times.
*

## Slide 43
Intel Core generation | Graphics generation | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Westmere | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 7th | HD 2500 | GT1 | 1 (6 EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Evolution of main features of Intel’s graphics families (based on [174]) -1
1.2 Evolution of desktop and laptop processors (9)

## Slide 44
Intel Core generation | Graphics generation | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Westmere | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 7th | HD 2500 | GT1 | 1 (6 EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Evolution of main features of Intel’s graphics families (based on [174]) -2
1.2 Evolution of desktop and laptop processors (10)

## Slide 45
Intel Core generation | Graphics generation | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Westmere | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 7th | HD 2500 | GT1 | 1 (6 EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Evolution of main features of Intel’s graphics families (based on [174]) -3
1.2 Evolution of desktop and laptop processors (11)

## Slide 46: 1.2 Evolution of desktop and laptop processors (12)
Example: A slice of the graphics unit of Haswell (6.5th gen. graphics)
1 slice (GT2): includs 20 EUs [199]

## Slide 47: 1.2 Evolution of desktop and laptop processors (13)
Block diagram of an EU of Haswell -1 [199]
Each EU has four functional units:
Two SIMD FPU units
1 Send unit (Load/Store) and
1 Branch unit.
An EU issues up to 4 instructions per cycle to the functional units.
*
SIMD: Single Instruction
Multiple Data

## Slide 48: 1.2 Evolution of desktop and laptop processors (14)
Block diagram of an EU of Haswell -2 [199]
Each SIMD FPUs can execute 4 SP FP They can execute MAD instructions (Multiply-Add)/cycle.
Thus an EU can execute 2 FPU x SIMD4 x 2 (MAD) = 16 SP FP operations/cycle.
The EU is 7-way multithreaded.
Each thread has 128 32 B registers.
One of the FPUs also supports FX operations (1/2/4/8/16/32 bit wide FX operations).
One of the FPUs also support transcendental math functions.

## Slide 49
Intel Core generation | Graphics generation | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Westmere | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 7th | HD 2500 | GT1 | 1 (6 EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Evolution of main features of Intel’s graphics families (based on [174])
1.2 Evolution of desktop and laptop processors (15)
*

## Slide 50
Intel Core generation | Graphics generation | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Westmere | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 7th | HD 2500 | GT1 | 1 (6 EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Evolution of main features of Intel’s graphics families (based on [174]) -4
1.2 Evolution of desktop and laptop processors (16)

## Slide 51
Intel Core generation | Graphics generation | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Westmere | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 7th | HD 2500 | GT1 | 1 (6 EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Evolution of main features of Intel’s graphics families (based on [174]) -5
1.2 Evolution of desktop and laptop processors (176)

## Slide 52: 1.2 Evolution of desktop and laptop processors (18)
Key features of the evolution of Intel’s integrated graphics families
Intel’s graphics implementations are subdivided into
graphics generations (5th to 9th) and
graphics technology levels (GT1-GT4).
Graphics generations are bound to the basic architectures.
The graphics technology levels indicate the number of graphics slices (replicable sets of
graphics EUs) within each graphics generation.
The number of graphics EUs is increasing more or less according to Moore’s rule
(from 12 in 2010 to 72 in 2015).
With the Haswell basic architecture graphics became eDRAM support (first 64 MB
then 128 MB)
There is continuous support of newer versions of graphics APIs and of OpenCL.
*

## Slide 53: 1.2 Evolution of desktop and laptop processors (19)
Graphics performance increase of subsequent Core generations [196]
Skylake
Broadwell
Haswell
Ivy Bridge
Sandy Bridge

## Slide 54
1.3 Evolution of HEDs (High-End desktops)
Notes: 54

## Slide 55: 1.3 Evolution of HEDs (High-End desktops) (1)
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smarphones
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smartphones
Desktops
Smarphones
Servers
Recent processor categories of Intel
Smartphones
Tablets
Atom lines
Xeon E7/E5/E3
Platinum/Gold etc.
Desktops/Laptops
(Client computing)
Core i7/i5/i3
(Basic architectures)
Atom lines
(+ LP Core models)
HEDs
(High-End Desktops)
Core i7/i9
(Extreme Edition
or X models)
1.3 Evolution of HEDs (High-End desktops)

## Slide 56: 1.3 Evolution of HEDs (High-End desktops) (2)
HEDs (High-End Desktops)
They aim at high performance desktops for hardcore gamers and graphics enthusiasts.
*

## Slide 57: 1.3 Evolution of HEDs (High-End desktops) (3)
Hardcore gamer scenario [221]

## Slide 58: 1.3 Evolution of HEDs (High-End desktops) (4)
Key features of Intel’s HED lines to support multiple (up to 4) discrete graphics cards:
1. Introduction -2
They typically provide vs. mainstream desktops
more PCIe lanes (either on the PCH or on the die)
more cores and
more memory channels (to appropriately service more processing resources)
as indicated on the next Figure.
*

## Slide 59: 1.3 Evolution of HEDs (High-End desktops) (5)
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachment | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Core 2 Extreme X6800 | 65 nm | 7/2006 | 2C | Via MCH | DDR3-1066 | 32 PCIe 2.0 on the X38 | 2 | X38 | 65 W | LGA 775
Core 2 Extreme QX 6xxx | 65 nm | 11/2006 | 2x2C |  |  |  |  |  | 130 W | LGA 775
 |  |  |  |  |  |  |  |  | 130 W | LGA 775
Core 2 Extreme QX 9650 (Penryn) | 45 nm | 11/2007 | 2x2C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 32 PCIe 2.0 on the X48 | 2 | X48 | 136 W | LGA 775
Core 2 Extreme QX 9770 (Penryn) | 45 nm | 3/2008 | 2x2C |  |  |  |  |  |  | 
1. G. Nehalem EE | 45 nm | 11/2008 | 4C | On-die MC | DDR3-1067 | 36 PCIe 2.0 on the X58 | 3 | X58 (Tylersburg) | 130 W | LGA 1366
Westmere EE | 32 nm | 3/2010 | 6C |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 130 W | LGA 1366
Sandy Bridge E | 32 nm | 11/2011 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 40 PCIe 2.0 on-die | 4 | X79 (Patsburg) | 130 W/ 150 W | LGA 2011
Ivy Bridge E | 22 nm | 9/2013 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1866 | 40 PCIe 3.0 on-die | 4 |  | 130 W | LGA 2011
Haswell E | 14 nm | 8/2014 | 8C |  | DDR4-2133 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Broadwell E | 14 nm | 5/2016 | 10C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2400 |  | 4 | X99 (Wellsburg) | 140 W | LGA_2011-3
Skylake X | 14 nm | 6/2017 | 18C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 140 W | LGA-2066
(Kaby Lake X) | 14 nm | 6/2017 | 4C |  | DDR4-2666 | 16 PCIe 3.0 on-die | 4 | X299 (Basin Falls) | 112 W | LGA-2066
Number of PCIe lanes
The above HED models and lines are unlocked.
*

## Slide 60: 1.3 Evolution of HEDs (High-End desktops) (6)
DT processors: 16 lanes
(1x16 or 2x8 or 1x8+2x4)
PCIe lanes provided on the processor die
HED processors: 40 lanes (typical)
(configurable, e.g. 2x x16 + 1x x8 or 4x x8)
PCIe 3.0 lanes
PCIe 2.0 lanes
PCIe generation
Mem.
P
Periph. Contr.
PCIe
2.0
x16/
2x x8
x16/
2x x8
Mem.
P
Periph. Contr.
PCIe
3.0
Intel 2. gen. Nehalem (Lynnfield) (4C), 2 MCh
with P55 (2009)
Intel Sandy Bridge (4C), 2 MCh with P67 (2011)
P55/P67
Z77/Z87/Z97/
Z170
Intel Ivy Bridge-E (6C), 4 MCh with X79 (2013)
Intel Haswell-E (8C) 4 MCh with X79 (2014)
Intel Broadwell-E (10C) 4 MCh with X99 (2016)
Intel Skylake-X (10C) 4 MCh with X299 (2017)
(44 PCIe lanes!)
Number of on-die memory channels and PCIe lanes provided on Intel's DT and HED lines
PCIe 3.0
40
configurable
lanes
Mem.
P
Periph. Contr.
X79/Z99/
X299
PCIe 2.0
40
configurable
lanes
Mem.
P
Periph. Contr.
X79
Intel Sandy Bridge-E (6C), 4 MCh with X79 (2011)
Intel Ivy Bridge (4C), 2 MCh with Z77 PCH (2012)
Intel Haswell (4C), 2 MCh with Z87 PCH (2013)
Intel Broadwell (4C), 2 MCh with Z97 PCH (2015)
Intel Skylake-S (4C), 2 MCh with Z170 PCH (2015)
*

## Slide 61: 1.3 Evolution of HEDs (High-End desktops) (7)
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachment | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Core 2 Extreme X6800 | 65 nm | 7/2006 | 2C | Via MCH | DDR3-1066 | 32 PCIe 2.0 on the X38 | 2 | X38 | 65 W | LGA 775
Core 2 Extreme QX 6xxx | 65 nm | 11/2006 | 2x2C |  |  |  |  |  | 130 W | LGA 775
 |  |  |  |  |  |  |  |  | 130 W | LGA 775
Core 2 Extreme QX 9650 (Penryn) | 45 nm | 11/2007 | 2x2C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 32 PCIe 2.0 on the X48 | 2 | X48 | 136 W | LGA 775
Core 2 Extreme QX 9770 (Penryn) | 45 nm | 3/2008 | 2x2C |  |  |  |  |  |  | 
1. G. Nehalem EE | 45 nm | 11/2008 | 4C | On-die MC | DDR3-1067 | 36 PCIe 2.0 on the X58 | 3 | X58 (Tylersburg) | 130 W | LGA 1366
Westmere EE | 32 nm | 3/2010 | 6C |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 130 W | LGA 1366
Sandy Bridge E | 32 nm | 11/2011 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 40 PCIe 2.0 on-die | 4 | X79 (Patsburg) | 130 W/ 150 W | LGA 2011
Ivy Bridge E | 22 nm | 9/2013 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1866 | 40 PCIe 3.0 on-die | 4 |  | 130 W | LGA 2011
Haswell E | 14 nm | 8/2014 | 8C |  | DDR4-2133 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Broadwell E | 14 nm | 5/2016 | 10C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2400 |  | 4 | X99 (Wellsburg) | 140 W | LGA_2011-3
Skylake X | 14 nm | 6/2017 | 18C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 140 W | LGA-2066
(Kaby Lake X) | 14 nm | 6/2017 | 4C |  | DDR4-2666 | 16 PCIe 3.0 on-die | 4 | X299 (Basin Falls) | 112 W | LGA-2066
Core counts
The above HED models and lines are unlocked.

## Slide 62
Remark
The Kaby Lake-X models in fact do not fit into the traditional HED line, they are actually the
highest performance models of the KabyLake line and are designated as mobile models.

## Slide 63: 1.3 Evolution of HEDs (High-End desktops) (8)
2006
2003
2010
2014
2016
2006
Evolution of the core counts in Intel's HED lines (Based on [222])
2017
Core 2
Extreme
X6800
Westmere EE
Haswell E
Broadwell E
Core 2
Extreme
QX6700
Skylake X
18
18 CORE
Number of cores
Pentium 4 EE
3.2

## Slide 64: 1.3 Evolution of HEDs (High-End desktops) (9)
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachment | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Core 2 Extreme X6800 | 65 nm | 7/2006 | 2C | Via MCH | DDR3-1066 | 32 PCIe 2.0 on the X38 | 2 | X38 | 65 W | LGA 775
Core 2 Extreme QX 6xxx | 65 nm | 11/2006 | 2x2C |  |  |  |  |  | 130 W | LGA 775
 |  |  |  |  |  |  |  |  | 130 W | LGA 775
Core 2 Extreme QX 9650 (Penryn) | 45 nm | 11/2007 | 2x2C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 32 PCIe 2.0 on the X48 | 2 | X48 | 136 W | LGA 775
Core 2 Extreme QX 9770 (Penryn) | 45 nm | 3/2008 | 2x2C |  |  |  |  |  |  | 
1. G. Nehalem EE | 45 nm | 11/2008 | 4C | On-die MC | DDR3-1067 | 36 PCIe 2.0 on the X58 | 3 | X58 (Tylersburg) | 130 W | LGA 1366
Westmere EE | 32 nm | 3/2010 | 6C |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 130 W | LGA 1366
Sandy Bridge E | 32 nm | 11/2011 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 40 PCIe 2.0 on-die | 4 | X79 (Patsburg) | 130 W/ 150 W | LGA 2011
Ivy Bridge E | 22 nm | 9/2013 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1866 | 40 PCIe 3.0 on-die | 4 |  | 130 W | LGA 2011
Haswell E | 14 nm | 8/2014 | 8C |  | DDR4-2133 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Broadwell E | 14 nm | 5/2016 | 10C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2400 |  | 4 | X99 (Wellsburg) | 140 W | LGA_2011-3
Skylake X | 14 nm | 6/2017 | 18C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 140 W | LGA-2066
(Kaby Lake X) | 14 nm | 6/2017 | 4C |  | DDR4-2666 | 16 PCIe 3.0 on-die | 4 | X299 (Basin Falls) | 112 W | LGA-2066
Number of memory channels
The above HED models and lines are unlocked.

## Slide 65: 1.3 Evolution of HEDs (High-End desktops) (10)
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachment | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Core 2 Extreme X6800 | 65 nm | 7/2006 | 2C | Via MCH | DDR3-1066 | 32 PCIe 2.0 on the X38 | 2 | X38 | 65 W | LGA 775
Core 2 Extreme QX 6xxx | 65 nm | 11/2006 | 2x2C |  |  |  |  |  | 130 W | LGA 775
 |  |  |  |  |  |  |  |  | 130 W | LGA 775
Core 2 Extreme QX 9650 (Penryn) | 45 nm | 11/2007 | 2x2C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 32 PCIe 2.0 on the X48 | 2 | X48 | 136 W | LGA 775
Core 2 Extreme QX 9770 (Penryn) | 45 nm | 3/2008 | 2x2C |  |  |  |  |  |  | 
1. G. Nehalem EE | 45 nm | 11/2008 | 4C | On-die MC | DDR3-1067 | 36 PCIe 2.0 on the X58 | 3 | X58 (Tylersburg) | 130 W | LGA 1366
Westmere EE | 32 nm | 3/2010 | 6C |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 130 W | LGA 1366
Sandy Bridge E | 32 nm | 11/2011 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 40 PCIe 2.0 on-die | 4 | X79 (Patsburg) | 130 W/ 150 W | LGA 2011
Ivy Bridge E | 22 nm | 9/2013 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1866 | 40 PCIe 3.0 on-die | 4 |  | 130 W | LGA 2011
Haswell E | 14 nm | 8/2014 | 8C |  | DDR4-2133 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Broadwell E | 14 nm | 5/2016 | 10C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2400 |  | 4 | X99 (Wellsburg) | 140 W | LGA_2011-3
Skylake X | 14 nm | 6/2017 | 18C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 140 W | LGA-2066
(Kaby Lake X) | 14 nm | 6/2017 | 4C |  | DDR4-2666 | 16 PCIe 3.0 on-die | 4 | X299 (Basin Falls) | 112 W | LGA-2066
Unlocked clock multiplier
The above HED models and lines are unlocked.

## Slide 66: 1.3 Evolution of HEDs (High-End desktops) (11)
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachment | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Core 2 Extreme X6800 | 65 nm | 7/2006 | 2C | Via MCH | DDR3-1066 | 32 PCIe 2.0 on the X38 | 2 | X38 | 65 W | LGA 775
Core 2 Extreme QX 6xxx | 65 nm | 11/2006 | 2x2C |  |  |  |  |  | 130 W | LGA 775
 |  |  |  |  |  |  |  |  | 130 W | LGA 775
Core 2 Extreme QX 9650 (Penryn) | 45 nm | 11/2007 | 2x2C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 32 PCIe 2.0 on the X48 | 2 | X48 | 136 W | LGA 775
Core 2 Extreme QX 9770 (Penryn) | 45 nm | 3/2008 | 2x2C |  |  |  |  |  |  | 
1. G. Nehalem EE | 45 nm | 11/2008 | 4C | On-die MC | DDR3-1067 | 36 PCIe 2.0 on the X58 | 3 | X58 (Tylersburg) | 130 W | LGA 1366
Westmere EE | 32 nm | 3/2010 | 6C |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 130 W | LGA 1366
Sandy Bridge E | 32 nm | 11/2011 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 40 PCIe 2.0 on-die | 4 | X79 (Patsburg) | 130 W/ 150 W | LGA 2011
Ivy Bridge E | 22 nm | 9/2013 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1866 | 40 PCIe 3.0 on-die | 4 |  | 130 W | LGA 2011
Haswell E | 14 nm | 8/2014 | 8C |  | DDR4-2133 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Broadwell E | 14 nm | 5/2016 | 10C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2400 |  | 4 | X99 (Wellsburg) | 140 W | LGA_2011-3
Skylake X | 14 nm | 6/2017 | 18C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 140 W | LGA-2066
(Kaby Lake X) | 14 nm | 6/2017 | 4C |  | DDR4-2666 | 16 PCIe 3.0 on-die | 4 | X299 (Basin Falls) | 112 W | LGA-2066
TDP (Thermal Design Power)
The above HED models and lines are unlocked.

## Slide 67: 1.3 Evolution of HEDs (High-End desktops) (12)
Key features of Intel’s HED lines (cont.):
Introduction -3
They are equipped with a large number of PCIe lanes (typically 32 to 44) to connect
multiple discrete graphics cards vs. 16 typical in desktops,
they do not provide integrated graphics, as it is assumed that the installation is intended
to provide high quality graphics by attaching discrete graphics cards,
*
they have more cores than desktops than graphics offers more parallelism than typical
desktop workloads,
they are unlocked and
HEDs have a higher TDP of 130 to 150 W vs. 65 to 95 W typical for DT processors.

## Slide 68
1.4 Evolution of high-end 4S/8S servers
Notes: 68

## Slide 69: 1.4 Evolution of high-end 4S/8S servers (1)
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smarphones
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smartphones
Desktops
Smarphones
Servers
Recent processor categories of Intel
Smartphones
Tablets
Atom lines
Xeon E7/E5/E3
Platinum/Gold etc.
Desktops/Laptops
(Client computing)
Core i7/i5/i3
(Basic architectures)
Atom lines
(+ LP Core models)
HEDs
(High-End Desktops)
Core i7/i9
(Extreme Edition
or X models)
1.4 Evolution of high-end 4S/8S servers

## Slide 70: 1.4 Evolution of high-end 4S/8S servers (2)
Server platforms classified according to the number of processors supported
2S (DP)
server platforms
Server platforms
Platforms for more than 4 or 8 sockets
2- processor server platforms
(2-socket server platforms)
4S/8S (MP)
server platforms
4/8-processor server platforms
(4/8-socket server platforms)
Server platforms for
more than the Intel
supported number of
sockets
(4 or 8 sockets)
They need third party
node controllers
Uniprocessor server platforms
(UP-server platforms)
1-processor server platforms
(1-socket server platforms)
Multiprocessor server platforms
Server platforms supporting more than one processor
(Multi-socket server platforms)
*

## Slide 71: 1.4 Evolution of high-end 4S/8S servers (3)
 | Core | Techn. | Intro. | High-end 4S/8S server processor lines | Core count | Chipset | Proc. socket
Truland MP | Pentium 4 MP Prescott | 90 nm | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 1C | E8500 + ICH5 | LGA 604
 | Pentium 4 Presc. | 90 nm | 11/2005 | 7000 (Paxville MP) | 2x1C | E8501 + ICH5 | 
 | Pentium 4 Presc. | 65 nm | 8/2006 | 7100 (Tulsa) | 2x1C |  | 
Caneland | Core2 | 65 nm | 9/2007 | 7200 (Tigerton DC) 7300 (Tigerton QC) | 2C 2x2C | E7300 (Clarksboro)+ 631x/632x ESB | LGA 604
 | Penryn | 45 nm | 9/2008 | 7400 (Dunnington) | 6C |  | 
Boxboro-EX | Nehalem | 45 nm | 3/2010 | 7500 (Beckton/ Nehalem-EX) | 8C | 7500 + ICH10 | LGA 1567
 | Westmere | 32 nm | 4/2011 | E7-8800 (Westmere-EX) | 10C |  | 
 | Sandy Bidge | 32 nm |  |  |  |  | 
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-8800 v2 (Ivy Bridge-EX) | 15C | C602J (Patsburg J) | LGA 2011-1
 | Haswell | 22 nm | 5/2015 | E7-8800 v3 (Haswell-EX) | 18C |  | 
 | Broadwell | 14 nm | 6/2016 | E7-8800 v4 (Broadwell-EX) | 24C |  | 
Purley | Skylake | 14 nm | 7/2017 | Platinum 8100 (Skylake-SP) | 28C | C620 (Lewisburg) | LGA 3647
Intel’s high-end 4S/8S server platforms built up of multicore processors -- Overview

## Slide 72: 1.4 Evolution of high-end 4S/8S servers (4)
 | Core | Techn. | Intro. | High-end 4S/8S server processor lines | Core count | Chipset | Proc. socket
Truland MP | Pentium 4 MP Prescott | 90 nm | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 1C | E8500 + ICH5 | LGA 604
 | Pentium 4 Presc. | 90 nm | 11/2005 | 7000 (Paxville MP) | 2x1C | E8501 + ICH5 | 
 | Pentium 4 Presc. | 65 nm | 8/2006 | 7100 (Tulsa) | 2x1C |  | 
Caneland | Core2 | 65 nm | 9/2007 | 7200 (Tigerton DC) 7300 (Tigerton QC) | 2C 2x2C | E7300 (Clarksboro)+ 631x/632x ESB | LGA 604
 | Penryn | 45 nm | 9/2008 | 7400 (Dunnington) | 6C |  | 
Boxboro-EX | Nehalem | 45 nm | 3/2010 | 7500 (Beckton/ Nehalem-EX) | 8C | 7500 + ICH10 | LGA 1567
 | Westmere | 32 nm | 4/2011 | E7-8800 (Westmere-EX) | 10C |  | 
 | Sandy Bidge | 32 nm |  |  |  |  | 
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-8800 v2 (Ivy Bridge-EX) | 15C | C602J (Patsburg J) | LGA 2011-1
 | Haswell | 22 nm | 5/2015 | E7-8800 v3 (Haswell-EX) | 18C |  | 
 | Broadwell | 14 nm | 6/2016 | E7-8800 v4 (Broadwell-EX) | 24C |  | 
Purley | Skylake | 14 nm | 7/2017 | Platinum 8100 (Skylake-SP) | 28C | C620 (Lewisburg) | LGA 3647
a) The rate of rising core counts in Intel's high-end 4S/8S server processors -1

## Slide 73: 1.4 Evolution of high-end 4S/8S servers (5)
a) The rate of rising core counts in Intel's high-end 4S/8S server processors -2
*
(P4)

## Slide 74: 1.4 Evolution of high-end 4S/8S servers (6)
Remarks to the rate of rising core counts in Intel's high-end 4S/8S server processors -1
(Not discussed)
As the Figure above demonstrates, the core count of Intel’s early L3-less 4S server
processors has doubled roughly biannually.
This is obvious, since the evolving IC technology allowed to double transistor counts
roughly in every new technology node.
Consequently, in L3-less processors twice as many transistors per technology node permit
the doubling of core counts also roughly biannually.
Model | Technology | Date of introduction | Core count | L3 cache | Transistors (million) | Die area (mm2)
7300 | 65 nm | 9/2007 | 2x2 | -- | 582 | 286
7400 | 45 nm | 8/2008 | 6 | 16 MB | 1900 | 503
Nehalem-EX | 45 nm | 3/2010 | 8 | 8x3 MB | 2300 | 513
Westmere-EX | 32 nm | 4/2011 | 10 | 10x3 MB | 2600 | 512
Ivy Bridge-EX | 22 nm | 2/2014 | 15 | 15x2.5 MB | 4310 | 541
Haswell-EX | 22 nm | 5/2015 | 18 | 18x2.5 MB | 5700 | 662
Broadwell-EX | 14 nm | 6/2016 | 24 | 24x2.5 MB | 7200 | 456
Table: Rising transistor counts in Intel's high-end 4S/8S server processsors
When L3 caches first appeared in the Xeon 7400 within Intel’s Core 2 based server
processors, the transistor count rose to 1.9 billion from 582 million in the L3-less Xeon
7300, as indicated in Table below.

## Slide 75: 1.4 Evolution of high-end 4S/8S servers (7)
Thermal
sensors
2 cores
2 cores
2 cores
4 MB LLC
4 MB LLC
4 MB LLC
4 MB LLC
3 MB MLC
3 MB MLC
3 MB MLC
Tags
Tags
Data pad
Address pad
Die plot of the Xeon 7400 MP implementing 16 MB L3 cache [215]
8 MB L3
3 MB L2/2 cores

## Slide 76: 1.4 Evolution of high-end 4S/8S servers (8)
However, to place twice as many cores onto the die with the same L3 size per core
in every technology node, would need to double this already high transistor count
in every technology node.
Remarks to the rate of rising core counts in Intel's high-end 4S/8S server processors -2
Model | Technology | Date of introduction | Core count | L3 cache | Transistors (million) | Die area (mm2)
7300 | 65 nm | 9/2007 | 2x2 | -- | 582 | 286
7400 | 45 nm | 8/2008 | 6 | 16 MB | 1900 | 503
Nehalem-EX | 45 nm | 3/2010 | 8 | 8x3 MB | 2300 | 513
Westmere-EX | 32 nm | 4/2011 | 10 | 10x3 MB | 2600 | 512
Ivy Bridge-EX | 22 nm | 2/2014 | 15 | 15x2.5 MB | 4310 | 541
Haswell-EX | 22 nm | 5/2015 | 18 | 18x2.5 MB | 5700 | 662
Broadwell-EX | 14 nm | 6/2016 | 24 | 24x2.5 MB | 7200 | 456
Table: Rising transistor counts in Intel's high-end 4S/8S server processors
Nevertheless, mainly due to power restrictions Intel could raise transistor counts on server
dies only at the modest rate of doubling roughly every four years, as above Table reveals,
leading to doubling core counts approximately every four years, as depicted in the above
Figure.
Recently, the nascent lengthening of the cadence of IC technology transitions also
contributes to reducing the rate at which the core count can be increased.

## Slide 77: 1.4 Evolution of high-end 4S/8S servers (9)
*
Core count
2006
2008
2010
2012
2014
2016
Year
7000
(90 nm)
7300
(65 nm)
7400
(45 nm)
Nehalem-EX
(45 nm)
Westmere-EX
(32 nm)
Ivy-Bridge-EX
(22 nm)
Broadwell-EX
(14 nm)
*
*
*
*
*
2
4
8
18
28
24
10
6
15
*
*
~2x/4 years
~2x/2 years
Emergence of
L3 caches
in the Core 2 line
*
*
Haswell-EX
(22 nm)
Skylake-SP
(14 nm)
*
7100
(65 nm
16 MB L3)
(P4)
(P4)
Remarks to the rate of rising core counts in Intel's high-end 4S/8S server processors -3

## Slide 78: 1.4 Evolution of high-end 4S/8S servers (10)
There are however, two anomalies to be mentioned.
First, the Xeon 7100 has less cores than expected by the trend for Intel’s early server
processors, simply due to the fact that it was implemented with a 16 MB L3 cache.
Second, the Xeon 7400 has already an L3 cache, nevertheless it fits to the trend line of
L3 cache-less processors.
The reason is a roughly doubled die area with reduced feature size vs. the preceding
Xeon 7300 (see Table above) which allows to implement a 16 MB L3 cache in addition to
the 6 cores without restricting the core count.
Model | Technology | Date of introduction | Core count | L3 cache | Transistors (million) | Die area (mm2)
7300 | 65 nm | 9/2007 | 2x2 | -- | 582 | 286
7400 | 45 nm | 8/2008 | 6 | 16 MB | 1900 | 503
Nehalem-EX | 45 nm | 3/2010 | 8 | 8x3 MB | 2300 | 513
Westmere-EX | 32 nm | 4/2011 | 10 | 10x3 MB | 2600 | 512
Ivy Bridge-EX | 22 nm | 2/2014 | 15 | 15x2.5 MB | 4310 | 541
Haswell-EX | 22 nm | 5/2015 | 18 | 18x2.5 MB | 5700 | 662
Broadwell-EX | 14 nm | 6/2016 | 24 | 24x2.5 MB | 7200 | 456
Table: Rising transistor counts in Intel's high-end 4S/8S server processsors
Subsequent server processors were then implemented nearly on the same die area
as the Xeon 7400, (as indicated in Table 1), so these processors fit already to the linear
trend with reduced slope.
Remarks to the rate of rising core counts in Intel's high-end 4S/8S server processors -3

## Slide 79
*
Transfer rate (MT/s)
50
100
500
Year
03
05
01
02
04
06
07
08
1000
3000
200
2000
~ 2*/4 years
DDR2
533
DDR2
667
DDR2 800
DDR3
1600
09
11
2010
12
13
15
DDR3
1067
2000

14
*
DDR3
1333
DDR3/1866
*
DDR
333
~ 2*/8 years
DDR
266
b) The rate of rising memory transfer rates in Intel’s DT and high-end server processors -1
x
x
x
x
*
DDR
400
DDR2
667
DDR3
1600
DDR3/4
1866
DDR
400
DDR3
1067
DT
4S/8S
2. Evolution of 4S/8S high-end servers (11)
Emergence of
DDR3 memory
16
17
*
*
*
*
*
*
x
x
DDR4
1866
DDR4
2666
Emergence of
DDR4 memory
IB
*
*
DDR4/2133
x
DDR4/2400

## Slide 80: 1.4 Evolution of high-end 4S/8S servers (12)
As the above Figure shows, in the course of the evolution of high-end 4S/8S servers
memory transfer rate has initially been doubled roughly every four years.
But after DDR3 memory emerged the growth rate of memory transfer rate slowed down
to doubling rougly every eight years due to the higher complexity of this technology.
Note that in the considered time interval memory transfer rate has always been risen
at a slower rate than core count, approximately at the half rate than the core count.
The rate of rising mem. transfer rates in Intel’s high-end 4S/8S server processors -2
*

## Slide 81: 1.4 Evolution of high-end 4S/8S servers (13)
The requirement for scaling the memory bandwidth with the core count
As each core may operate independently from each other the memory bandwidth provided
needs to be linearly scaled with the core count, i.e. a processor with n-times more cores
as a reference platform requires n-times higher bandwidth as the reference platform.
*

## Slide 82: 1.4 Evolution of high-end 4S/8S servers (14)
Implication of the fact that memory transfer rates are rising slower than core counts
in servers
Over generations both the core count and the memory transfer rate are raising.
But the memory transfer rate of the reference platform rises slower than the core count,
thus the per core memory bandwidth will decrease since the memory bandwidth amounts to
the product of the transfer rate and the width of the memory interface (assuming that
no other changes become effective).
In other words, in the course of processor evolution a memory bandwidth gap arises that
needs to be removed by implementing appropriately more memory channels.
Thus removing the memory bandwidth gap more memory channels are needed,
this is the driving force of the evolution of server memory subsystems.
Since it is not at all a straightforward task to raise the number of memory channels,
one of the focal points of server evolution is how to resolve the memory bandwidth gap
by enhancing the memory subsystem.
In the chapter on high-end 4S/8S servers we will discuss possible avenues of coping
with this point.
*

## Slide 83
1.5 Evolution of tablet and smartphone processors
Notes: 83

## Slide 84: 1.5 Evolution of tablet and smartphone processors (1)
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smarphones
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smartphones
Desktops
Smarphones
Servers
Recent processor categories of Intel
Smartphones
Tablets
Atom lines
Xeon E7/E5/E3
Platinum/Gold etc.
Desktops/Laptops
(Client computing)
Core i7/i5/i3
(Basic architectures)
Atom lines
(+ LP Core models)
HEDs
(High-End Desktops)
Core i7/i9
(Extreme Edition
or X models)
1.5 Evolution of tablet and smartphone processors

## Slide 85
High performance/power
(e.g. GFLOPS/Watt)
Traditional processors
Tablets and smartphones
Low power
(Watt)
(Number of operating hours)
With the advent of mobile devices (about 2006) a new design paradigm arose for those devices.
Mobile devices require long operating hours i.e. low power consumption, this is contrast to the
design paradigm of traditional processors, as indicated below.
1.5 Evolution of tablet and smartphone processors (1b)
Changing the design paradigm for implementing mobile processors
*

## Slide 86: 1.5 Evolution of tablet and smartphone processors (2)
Key requirements for low power microarchitectures
Low processor clock frequency
Narrow microarchitecture
Key requirements at the introduction of mobile, i.e. low power microarchitectures
*

## Slide 87: 1.5 Evolution of tablet and smartphone processors (3)
2005
2007
2010
2009
(A9 replacement
for low-end
devices)
32-bit
Example: Width of ARM’s early, 32-bit CPUs used in most tablets and smartphones [10]
a) Low power CPUs need narrow microarchitectures
*

## Slide 88: 1.5 Evolution of tablet and smartphone processors (4)
By contrast:
Intel’s and AMD’s recent processor lines
aims at high performance/power (in terms of GFLOPS/Watt)
accordingly
have 4-wide microarchitectures, as the next example shows:
64-bit
Example: Width of Intel’s Core 2 to Haswell processors underlying servers to laptops [10]
*

## Slide 89: 1.5 Evolution of tablet and smartphone processors (5)
Consequences for Intel and AMD-1
Intel’s and AMD’s traditional microarchitectures are not suited for mobile devices.
Both Intel and AMD conceived, designed and introduced new, narrow (e.g. 2-wide) low-power microarchitectures.
*

## Slide 90: 1.5 Evolution of tablet and smartphone processors (6)
Emergence of Intel’s Atom line aiming for tablets and smartphones (Based on [2])
2008
2-wide
in-order
4-wide
out-of-order
2-wide
in order
2-wide
out-of-order
2-wide
in-order
2-wide
out-of-order
2-wide
out-of-order
3-wide
out-of-order
5

## Slide 91: 1.5 Evolution of tablet and smartphone processors (6b)
Intel’s Atom-based smartphone platforms (based on [276])
Eul H., & Bell M., Mobile at Intel, Investor Meeting 2012, Intel,
http://www.cnx-software.com/pdf/Intel_2012/2012_Intel_Investor_Meeting_Eul_Bell.pdf
Clover Trail+
(2013)
Medfield
(2012)
Merrifield
(2014)
Moorefield
(2014)
Lexington
(2013)
Slayton
(2014)
Z2520-2580
2x Saltwell
32 nm
+XMM 6268/6360/7160
Z2420
1x Saltwell
32 nm
+XMM 6265
Z2460/2480
1x Saltwell
32 nm
+XMM 6260
Z34x0
2x Silvermont
22 nm
+XMM 7160/7260
Z3xxx
2x Silvermont
22 nm
+A-GOLD 620
Z35xx
4x Silvermont
22 nm
+XMM 7260/2/35
Performance (not to scale)
Morestown
(2010)
Z6xx
1x Bonnell
45 nm
+Wireless
module
Riverton
(2015)
SoFIA
(x3 3G/LTE)
(2015)
Z3xxx
2x Airmont
14 nm
Integrated
LTE modem
C31xx/32xx/34xx
2x/4x Silvermont
28 nm
Integrated LTE
3G/4G modem
Planned, not mplemented
Cancelled
in 04/2016
Planned, not implemented
Morganfield
(2016)
Z5xxx
4x Goldmont
14 nm
+XMM 7360
Cancelled
in 04/2016

## Slide 92: 1.5 Evolution of tablet and smartphone processors (6c)
2014
4/2014
2-wide
out-of-order
2-wide
out-of-order
2-wide
out-of-order
4-wide
out-of-order
Emergence of AMD's Cat line aiming for tablets and smartphones (Based on [2])

## Slide 93
b) Low power CPUs need to be operated at low base clock frequencies
High base clock frequency
(typically 2-4 GHz)
Traditional CPUs
Mobile CPUs
Relative low base clock frequency
(typically 1-2 GHz)
( Dd = const x fc x V2, in addition higher fc requires about linearly higher higher V)
1.5 Evolution of tablet and smartphone processors (7)
*

## Slide 94
TDP (W) | No. of cores | Graphics | No. of graphics EUs | eDRAM | Base frequency (GHz)
4.5 | 2 | HD 515 | 18 | -- | 1.2
15 | 2 | HD 540 | 48 | 64 MB | 2.2
15 | 2 | HD 520 | 24 | -- | 2.6
28 | 2 | HD 550 | 48 | 64 MB | 3.3
35 | 4 | HD 530 | 24 | -- | 2.8
45 | 4 | HD 530 | 24 | -- | 2.9
65 | 4 | HD 530 | 24 | -- | 3.4
91 | 4 | -- | -- | -- | 4.2
Example: The max. base frequency of Skylake models resulting in different TDPs and
configurations (Based on data from [202])
Note that low TDP can be achieved first of all by reducing the core frequency and limiting
the computer resources (cores, GPU EUs) provided.
1.5 Evolution of tablet and smartphone processors (8)
*

## Slide 95: 1.5 Evolution of tablet and smartphone processors (9)
Worldwide market share of smartphone and tablet application processors in 2015
(based on revenue) [217]
Smartphone application processors worldwide market share 2015 (revenue) | 
Qualcomm (USA) | 42 %
Apple (USA) | 21 %
MediaTek (Taiwan) | 19 %
Samsung (S. Korea) | 
Spreadtrum (China) | 
Tablet application processors worldwide market share 2015 (revenue) | 
Apple (USA) | 31 %
Qualcomm (USA) | 16 %
Intel (USA) | 14 %
MediaTek (Taiwan) | 
Samsung (S. Korea) | 
[Source: Related press releases of Strategy Analytics]
*

## Slide 96: 1.5 Evolution of tablet and smartphone processors (10)
Intel's withdrawal from the smartphone and mobil market [216]
In 4/2016 Intel announced their withdrawal from the mobil market.
Intel's statement says:
"I can confirm that the changes included canceling the Broxton platform as well as SoFIA
3GX, SoFIA LTE and SoFIA LTE2 commercial platforms to enable us to move resources
to products that deliver higher returns and advance our strategy.
These changes are effective immediately."
At the same time Intel laid off about 12000 employees (~ 11 % of their workforce).
*

## Slide 97: 1.5 Evolution of tablet and smartphone processors (11)
AMD’s cancellation of their Cat line in 2015
The last core of AMD's Cat line was the Puma+ core (launched in 6/2015 in the
Carrizo-L APU).
In AMD's 2016 Mobility roadmap there is no sign of an APU powered by the Puma+ core
or a derivative of it belonging to the Cat line.
Instead AMD has been placed emphasis on the Zen architecture that has been launched
in 2017.
*

## Slide 98: 1.5 Evolution of tablet and smartphone processors (12)
NVidia's leaving the smartphone and tablet market in June 2016 [81]
In 6/2016 (at Computex) NVIDIA's CEO J. Huang declared the firm's leaving the
smartphone and tablet market by saying:
: “We are no longer interested in that market”. He adds, “Anybody can build smartphones,
and we’re happy to enjoy these devices, but we’ll let someone else build them”.
Instead NVIDIA became interested in designing in-car computers and car infotainment
systems.

## Slide 99
2. The Core 2 line
2.1 Introduction
2.2 Major innovations of the Core 2 line
2.4 Die plot of the Core 2
2.5 Overview of Core 2 based processor lines
2.3 Performance leadership change between
Intel and AMD achieved by the Core 2
(Not discussed)
Notes: 99

## Slide 100
2.1 Introduction
Notes: 100

## Slide 101: 2.1 Introduction (1)
2.1 Introduction-1
The next line became based primarily on the Pentium M – Intel’s first mobile line
since for its designs dissipation reduction was a key issue.
(The Pentium M line was a 32-bit line with 3 subsequent cores, designed at
Intel’s Haifa Research and Development Center) thus the Core 2 was developed also there.
The Pentium 4 line was cancelled due to unmanageable high dissipation figures
of its third core (the 90 nm Prescott core)
(caused primarily by the design philosophy of the line
that preferred clock frequency over core efficiency for increasing performance).
The Haifa team had no experience with multithreading.
The Core microarchitecture does not support multithreading.
For the development of the next processor line dissipation became the key design issue.

## Slide 102: 2.1 Introduction (2)
Figure : Intel’s Tick-Tock development model (Based on [1])
Figure 4.1.1: Intel’s Tick-Tock development model (Based on [1])
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
1. gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
Skylake
New
Microarchi.
14 nm
TOCK
6. gen.
The Core 2 is Intel’s 1. generation new microarchitecture, it is using 65 nm line width.
First delivered in 6/2006.
2.1 Introduction-2

## Slide 103: 2.1. Introduction (3)
The Core 2 line -1
2 YEARS
Key new features of the ISP
and the microarchitecture
New microarch.: 4-wide core,
128-bit SIMD FX/FP EUs,
shared L2 , no HT
11/2007
01/2006
65nm
TICK Pentium 4 ( Cedar Mill)
Pentium D (Presler)
TOCK Core 2
07/2006
11/2008
New microarch.: 256-bit (FP) AVX,
ring bus, integrated GPU
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
New microarch.: 256-bit (FX) AVX2,
L4 cache (discrete eDRAM), TSX
06/2013
09/2014
Shared Virtual Memory
10/2015
New microarch.: 5-wide core,
ISP, Memory Side L4 cache, no FIVR
In package integrated GPU
14nm
4 YEARS
TICK Broadwell
TOCK Skylake
New microarch.: 4 cores, integr. MC,
QPI, private L2, (inclusive) L3, HT
TOCK Coffee Lake
TOCK Kaby Lake
08/2016
10/2017
2 YEARS
10nm
TICK Cannonlake
TOCK Icelake
05/2018
??/2019
?? YEARS
Optane memory, in KBL G series:
in package integr. CPU, GPU, HBM2
AVX512
(USB Gen. 2, integr. conn., Optane 2)
Figure is based on [3])

## Slide 104: 2.1. Introduction (3b)
2 YEARS
Key new features
in power management
11/2007
01/2006
65nm
TICK Pentium 4 ( Cedar Mill)
Pentium D (Presler)
TOCK Core 2
07/2006
11/2008
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
06/2013
09/2014
10/2015
14nm
4 YEARS
TICK Broadwell
TOCK Skylake
TOCK Coffee Lake
TOCK Kaby Lake
08/2016
10/2017
2 YEARS
10nm
TICK Cannonlake
TOCK Icelake
05/2018
??/2019
Clock gating, PECI,
Platform Thermal Control by
3. party controller
EDAT
Integrated Power Gates, PCU,
Turbo Boost
Turbo Boost 2.0
FIVR
2. gen. FIVR
Speed Shift Technology,
Duty Cycle control, No FIVR
(except Skylake X)
Speed Shift Technology v2
*
In H-series: TVB
(Thermal Velocity Boost)
The Core 2 line -2
Figure is based on [3])

## Slide 105
2.2 Major innovations of the Core 2 line
2.2.1 4-wide core
2.2.3 Smart L2 cache
2.2.4 Innovations in power management
2.2.2 128-bit SIMD and FP units
Notes: 105

## Slide 106: 2.2.1 4-wide core (1)
2.2 Major innovations of the Core 2 line
2.2.1 4-wide core
This is the key benefit of the Core 2 family.
By contrast
both Intel’s previous Pentium 4 family and AMD’s K8 have only 3-wide cores,
as the next Figures show.
It means 4-wide front end and retire unit.

## Slide 107: 2.2.1 4-wide core (2)
Figure 2.2.1.1: Block diagram of Intel’s Core 2 microarchitecture [3]

## Slide 108: 2.2.1 4-wide core (3)
Retire width: 3 instr./cycle
Figure 2.2.1.2: Block diagram of Intel’s Pentium 4 microarchitecture [5]

## Slide 109: 2.2.1 4-wide core (4)
Figure 2.2.1.3: Block diagram of AMD’s Athlon microarchitecture [4]

## Slide 110: 2.2.2 128-bit wide SIMD and FP units (1)
a) Overview of the x86 ISA extensions in Intel’s processor lines
2.2.2 128-bit wide SIMD and FP units
They aim at providing enhanced media support.

## Slide 111: 2.2.2 128-bit wide SIMD and FP units (2)
Advanced Encryption Standard
Advanced Vector Extension
Fused Multiply-Add instr.
Streaming SIMD Extensions
MultiMedia eXtensions
Northwood (Pentium 4)
Ivy Bridge
Pentium III
Pentium 4
Core 2
Overview of Intel’s x86 ISA extensions (based on [18])

## Slide 112: 2.2.2 128-bit wide SIMD and FP units (3)
Norhwood
Northwood (Pentium4)
Northwood (Pentium4)
8 MM registers (64-bit),
aliased on the FP Stack registers
8 XMM registers (128-bit)
16 XMM registers (128-bit)
16 YMM registers (256-bit)
Ivy Bridge
Pentium MMX
Pentium 4
Core 2
Pentium III
Register spaces provided by Intel’s x86 ISA extensions (based on [18])

## Slide 113: 2.2.2 128-bit wide SIMD and FP units (4)
Illustration of the available SIMD register spaces of the MMX to SSE3/SSSE3 ISA
extensions in 32- and 64-bit ISAs [162]

## Slide 114: 2.2.2 128-bit wide SIMD and FP units (5)
Norhwood
Northwood (Pentium4)
128-bit FX, FP SIMD with
32/16/8-bit FX, 32-bit FP ops.
Support of MM/3D
DSP-oriented FP enhancements,
enhanced thread manipulation
Diverse arithmetic enhancements
64-bit FX SIMD with
32/16/8-bit operands (ops)
Support of MM
128-bit FX, FP SIMD with
64/32/16/8-bit FX, 64/32-bit FP,
Support for MPEG-2, video, MP3
Media acceleration
(video encoding, MM, gaming)
Accelerated string/text manip.,
appl. targeted acceleration
Accelerated encription operations
256-bit FP SIMD with
64/32-bit FP
Ivy Bridge
Pentium III
Pentium 4
Core 2
Intel’s x86 ISA extensions - the operations introduced (based on [18])

## Slide 115: 2.2.2 128-bit wide SIMD and FP units (6)
SSSE3 provide 32 instructions (represented by 14 mnemonics) to accelerate computations on
packed integers.
These include:
Overview of the Supplemental Streaming SIMD Extension (SSSE3) of the Core 2 ISA
[161]
• Twelve instructions that perform horizontal addition or subtraction operations (operations
on adjacent numbers.
• Six instructions that evaluate absolute values.
• Two instructions that perform multiply and add operations and speed up the evaluation
of dot products.
• Two instructions that accelerate packed-integer multiply operations and produce integer
values with scaling.
• Two instructions that perform a byte-wise, in-place shuffle according to the second
shuffle control operand.
• Six instructions that negate packed integers in the destination operand if the signs of the
corresponding element in the source operand is less than zero.
• Two instructions that align data from the composite of two operands.

## Slide 116: 2.2.2 128-bit wide SIMD and FP units (7)
Northwood (Pentium 4)
1 full + 1 simple (moves/stores)
64-bit FP/SSE EUs
2 x 128-bit FP EUs +
3 x 128-bit SSE EUs
256-bit SSE EUs
2 x 32-bit FX MMX EUs
2 x 32-bit MMX,
2 x 32-bit SSE EUs
Ivy Bridge
Pentium III
Pentium 4
Core 2
SIMD execution resources in Intel’s basic processors (based on [18])

## Slide 117: 2.2.2 128-bit wide SIMD and FP units (8)
The Core 2 has 128-bit wide and more FP and SSE execution units than Pentium 4 or AMD’s K8,
as detailed below.
b) Contrasting the number of 128-bit wide execution units in Intel’s Pentium 4, Core 2
and AMD’s K8 -1
The next Figure demonstrates it.
Core 2
two 128-bit FP units
three 128-bit SSE units
Pentium 4
single 64-bit FP/SSE unit
single 64-bit FP/SSE move unit
AMD K8
two 64-bit FP/SSE units
single 64-bit FP/SSE move unit

## Slide 118: 2.2.2 128-bit wide SIMD and FP units (9)
FP/SSE
K8 Execution Units
b) Contrasting the number of 128-bit wide execution units in Intel’s Pentium 4, Core 2
and AMD’s K8 -2 [159], [160]

## Slide 119: 2.2.2 128-bit wide SIMD and FP units (10)
Core 2’s achieved performance boost for gaming apps vs. AMD’s Athlon 64 FX60 [13]

## Slide 120: 2.2.3 Shared L2 cache (1)
Pentium 4-based DCs
Core 2-based DCs
2.2.3 Shared L2 cache
Core1
Core2
L2 Cache
L2 Cache
Core1
Core2
L2 Cache
Figure 2.2.3.1: Core’s shared L2 cache vs. Pentium 4’s private L2 caches
Private
Shared
In the Core 2 Intel makes use a shared L2 cache instead of private L2 caches and designates it
as smart L2 cache, as shown below.

## Slide 121: 2.2.3 Shared L2 cache (2)
Benefits of shared caches vs. private caches
Dynamic cache allocation to the individual cores
Data sharing (no replicated data)
+ 2x bandwidth to L1 caches.

## Slide 122: 2.2.3 Shared L2 cache (3)
Drawbacks of shared caches
Shared caches combine memory access patterns
Reduce the efficiency of hardware prefetching vs private caches.
Choice between shared and private caches
Design decision depending on
whether benefits or drawbacks dominate as far as performance is concerned.
Trend
Core 2 prefers a shared L2 cache
Nehalem prefers private L2 caches
POWER5 prefers shared L2 cache
POWER6 prefers private L2 caches
This trend is due to the fact that efficient data prefetching became more important than
dynamic cache allocation or data sharing.

## Slide 123: 2.2.3 Shared L2 cache (4)
Intel’s first hardware prefetcher appeared subsequently in the Pentium 4 family,
associated with the L2 cache (one instruction and one data prefetcher (11/2000).
Principle of operation of the L2 hardware prefetcher
it monitors data access patterns and prefetches data automatically into the L2 cache,
it attempts to stay 256 bytes ahead of the current data access location,
the prefetcher remembers the history of cache misses to detect concurrent,
independent data streams that it tries to prefetch ahead of its use.
Remarks
Intensive use of hardware prefetchers -1 [9]
Intel’s first on-die L2 cache debuted only about two years earlier (8/1998),
in the second core of the Pentium II based Celeron line (called the Mendocino core,
built on 250 nm technology, with an L2 size of 128 KB)1,2.
1 The first Celeron model debuted in 4/1998, it was the low cost alternative to Pentium II,
and was designated as Cavington.
It was manufactured on 250 nm, run at 266 MHz, did not include an L2 cache and had 7.5 mtrs.
The second core of the Celeron line was launched in 8/1998 already with an L2 cache, run
at 266 and 300 MHz and incorporated 19,2 mtrs.
2Note: The debut of L2 was corrected in 29/10/2014.

## Slide 124: 2.2.3 Shared L2 cache (5)
8 prefetchers in the two-core processor
2 data and 1 L1 instruction prefetchers per core,
able to handle multiple simultaneous patterns.
2 prefetchers in the L2 cache
tracking multiple access patterns per core.
Intensive use of hardware prefetchers -2 [11]

## Slide 125: 2.2.3 Shared L2 cache (6)
Figure 2.2.3.2: Hardware prefetchers within the Core 2 microarchitecture [11]
Hardware prefetchers in the Core 2 microarchitecture

## Slide 126: 2.2.4 Innovations in power management (1)
2.2.4 Innovations in power management
Shutting off not needed functional units of the processor
Platform Thermal Control

## Slide 127: 2.2.4 Innovations in power management (2)
Green units not needed
for the given operation,
they can be shut off.
Shutting off not needed functional units of the processor by clock gating [11]

## Slide 128: 2.2.4 Innovations in power management (3)
Platform Thermal Control [11], [20]
Digital
Thermal Sensors
(DTS) on the dies,
instead of
analog diodes,
providing
digital data,
scanned by
dedicated logic.
(Platform Environment Control Interface)
A single wire proprietary interface with
transfer rates of 2 kbit/s-2 Mbit/s)
DTSs report the difference between the
current temperature and the throttle point,
at which the processor reduces speed.
PECI

## Slide 129: 2.2.4 Innovations in power management (4)
Possible solution for the Platform Thermal Control Manager [88]
Figure 2.2.4.1: The aSC7621 hardware monitor with fan control and PECI from Andigilog
(Remote Sensor)
(Remote Sensor
CPU/Graphics)
(ASIC (Application Specific IC/Microcontroller)

## Slide 130
2.3 Performance leadership change between Intel and AMD achieved by the Core 2
Notes: 130

## Slide 131: 2.3 Performance leadership change between Intel and AMD (1)
AMD’s K8-based processors became the performance leader, first of all on the DP and MP
server market, where the 64-bit direct connect architecture has clear benefits
vs Intel’s 32-bit Pentium 4 based processors using shared FSBs to connect processors
to north bridges.
integrated memory controllers and
high speed point-to-point serial buses (the HyperTransport bus)
used to connect processors to processors and processors to south bridges.
Performance leadership change between Intel and AMD achieved by the Core 2
In 2003 AMD introduced their K8-based processors implementing
the 64-bit x86 ISA and
the direct connect architecture concept, that includes

## Slide 132: 2.3 Performance leadership change between Intel and AMD (2)
Figure 2.3.1: DP web server performance comparison: AMD Opteron 248 vs. Intel Xeon 2.8 [6]
Example 1: DP web-server performance comparison (2003)

## Slide 133: 2.3 Performance leadership change between Intel and AMD (3)
“In the extensive benchmark tests under Linux Enterprise Server 8 (32 bit as well as 64 bit),
the AMD Opteron made a good impression.
Especially in the server disciplines, the benchmarks (MySQL, Whetstone, ARC 2D, NPB, etc.)
show quite clearly that the Dual Opteron puts the Dual Xeon in its place”.
Example 2: Summary assessment of extensive benchmark tests contrasting
dual Opterons vs dual Xeons (2003) [7]

## Slide 134: 2.3 Performance leadership change between Intel and AMD (4)
two 128-bit FP units and three 128-bit SSE units compared to
This situation has completely changed in 2006 when Intel introduced their Core 2
microarchitecture,
Intel regained performance leadership vs AMD.
This and further enhancements of the Core microarchitecture, detailed subsequently,
resulted in record breaking performance figures.
a 4-wide front-end and retire unit compared to the 3-wide K8,
The Core 2 has
two 64-bit FP/SSE units and a single 64-bit FP/SSE move unit available in the K8.

## Slide 135: 2.3 Performance leadership change between Intel and AMD (5)
Webserver Performance |  |  |  |  | 
 | MSI K2-102A2M Opteron 275 | MSI K2-102A2M Opteron 280 | Opteron 280 vs. Opteron 275 | Extrapolated Opteron 3 GHz | Xeon 5160 3 GHz
Jsp - Peak | 144 | 154 | 7% | 182 | 230
AMP - Peak | 984 | 1042 | 6% | 1178 | 1828
Jsp: Java Server Page performance
AMP: Apache/MySQL/PHP
Example: DP web-server performance comparison (2006)
Figure 2.2.1.8: DP web server performance comparison:
AMD Opteron 275/280 vs. Intel Xeon 5160 [8]
Remark
Both web-server benchmark results were published from the same source (AnandTech)

## Slide 136
2.4 Die plot of the Core 2
Notes: 136

## Slide 137: 2.4 Die plot of the Core 2 (1)
143 mm2
291 mtrs
2.4 Die plot of the Core 2 [163]

## Slide 138
2.5 Overview of Core 2 based processor lines
Notes: 138

## Slide 139: 2.5 Overview of Core 2 based processor lines (1)
2.5 Overview of Core 2 based processor lines
Servers
DP-Servers
MP-Servers
51xx, 2C Woodcrest, 6/2006
53xx, 2x2, Clowertown, (2xWoodcrest) 11/2006
72xx, 2C, Tigerton DC, (2xMP-enhanced SC Woodcrest) 9/2007
73xx, 2x2C, Tigerton QC, (2xMP-enhanced DC Woodcrest) 9/2007
UP-Servers
30xx, 2C, Conroe, 9/2006
30xx, 2C, Allendale 1/2007
32xx, 2x2C, Kentsfield (2xConroe) 1/2007
Mobiles
T5xxx/T7xxx, 2C ,Merom 8/2006
Based on [43]
Desktops
E6xxx/E4xxx, 2C, Core 2 Duo, (Conroe) 7/2006
X6800 Core 2 Extreme, 2C, (Conroe) 7/2006
E6xxx/E4xxx, Core 2 Duo, 2C, (Allendale) 1/2007
Q6xxx Core 2 Quad, 2x2C (Kentsfield) (2xConroe) 1/2007
QX6xxx Core 2 Extreme Quad, 2x2C, (Kentsfield XE) 11/2006

## Slide 140: 2.5 Overview of Core 2 based processor lines (2)
Example Core 2 system architecture [223]

## Slide 143
Számítógép architektúrák III. BSc 2009. december 22.