## Slide 1
Dezső Sima
Nov. 2018
(Ver. 1.0)
 Sima Dezső, 2018
Interconnects

## Slide 2
1. Functional classification of interconnects
In the lecture only Section 1. will be discussed.

## Slide 3: 1. Functional classification of interconnects (1)
1. Functional classification of interconnects
Interconnects are the skeletons of processors, processor platforms or even
processor clusters.
There are however, a large number of different interconnects used.
Subsequently, we give a possible classification used also in discussing this
subject.

## Slide 4: 1. Functional classification of interconnects (2)
Intra-processor
interconnects
Cluster
interconnects
Functional classification of interconnects
Inter-processor
interconnects
P
Per./
IO
GPU
Disp
M
.
Functional classification of interconnects
Interconnects the functional
units of a processor
Interconnects processors
within a server
(e.g. DP/MP servers) [2]
Interconnects nodes
(e.g. 2P/4P servers) of a processor cluster [3]

## Slide 5: 1. Functional classification of interconnects (3)
On-die intra-processor interconnects
Off-die intra-processor interconnects
Intra-processor interconnects
Used to interconnect
functional units of a processor off-die
Used to interconnect
functional units of a processor on-die
P
NB
SB
Per./IO
GPU
Per./IO
M
Per./IO
Ring bus
MC
Per.
---
CC
--
A
IO
--
CC: Core Cluster
MC: Memory Controller
Intra-processor interconnects

## Slide 6: 1. Functional classification of interconnects (4)
Bus-based
off-die interconnects
(in the 1980’/1990’s)
E.g. Intel’s early desktop platforms (since 1981)
Transactions on a shared bus.
.
Chipset-based
off-die interconnects
(since about 2000)
P
NB
SB
Per./IO
GPU
Per./IO
M
Per./IO
Transactions on a set of dedicated links.
Multiple transactions at a time.
E.g. Intel’s Pentium 4 or early Core 2-based platforms (2000/2006)
Off-die intra-processor interconnects (discussed)
8088/286/386
Processor
Memory/
Bus controller
Main memory
KBD
FD
Adapter
Monitor
Adapter
WD
Adapter
PP
Adapter
SP
Adapter
ISA
Multi-I/O
card
(DRAM/FPM)
I/O devices
Off-die intra-processor interconnects

## Slide 7: 1. Functional classification of interconnects (5)
Shared bus
based interconnects
Crossbar-based
interconnects
AHB based SoCs
(non CC, ~2001) [8]
On-die intra-processor interconnects
PL-300 interconnect
(non CC, on AXI3, 2004)
through the CCI 550 interconnect
(CC, on ACE, 2015)
Examples
Intel
ARM
Nehalem (CC, on QPI, 2008)
On-die intra-processor interconnects -1
CC: Cache Coherent
P
GPU
M
Per./IO
---
---
Bus
Crossbar
M
Per.
Core
GPU
--
--
Higher
performance
for higher nc

## Slide 8: 1. Functional classification of interconnects (6)
Ring bus-based
interconnect topology
Ring
MC
Per.
---
CC
--
A
IO
--
2D mesh-based
interconnect topology
CMN-6xx Interconnect for servers
(CC, on CHI, 2017)
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
CC
CC
CC
CC
A
A
CC
CC
A
MC
MC
MC
MC
R
R
R
R
R
A
A
A
MC
MC
IO
IO
IO
IO
IO
IO
P
P
P
P
P
P
On-die interconnects -2
*
CC: Core Cluster
A: Accelerator (e.g. GPU, NPU)
nc: Core count
Topology of on-die interconnects
CCN-5xx interconnect for servers
(CC, on CHI, 2012)
Examples
Intel
ARM
Skylake-SP for servers
(CC, UPI, 2017)
Knights Landing for AI, (2016)
Sandy Bridge (CC, on QPI, 2011)
Less cost
for higher nc
Shorter
access time
for higher nc

## Slide 9
2. Intra-processor interconnects
2.1 Overview of intra-processor interconnects
2.2 Off-die intra-processor interconnects
2.3 On-die intra-processor interconnects
2.4 Use of both off-die and on-die interconnects

## Slide 10
2.1 Overview of intra-processor interconnects

## Slide 11: 2.1 Overview of intra-processor interconnects (1)
P
Per./
IO
GPU
Disp
M
.
2.1 Overview of intra-processor interconnects -1
Intra-processor
interconnects
Cluster
interconnects
Main types of system interconnects
Inter-processor
interconnects
Interconnects the functional
units of a processor
Interconnects processors
within a server
(e.g. DP/MP servers) [2]
Interconnects nodes
(e.g. 2P/4P servers) of a processor cluster [3]

## Slide 12: 2.1 Overview of intra-processor interconnects (2)
P
Per./
IO
GPU
Disp.
M
Overview of intra-processor interconnects -2
They provide the links required within a single processor platform, as indicated in the
Figure below.
Figure: The intra-processor interconnect provides the necessary links
within a single processor platform
Note
In case of multicores the intra-processor interconnect needs to provide
interconnections between the cores or core clusters (if core clusters are used).

## Slide 13: 2.1 Overview of intra-processor interconnects (3)
a) Use of individual CPU cores or CPU core clusters (CC) in multicore processors
b) Support of cache coherency (this aspect will not be discussed)
c) Implementing intra-processor interconnects off-die, on-die or even both
off-die and on-die
Design aspects affecting the implementation of the intra-processor
interconnect in multicore processors
Support of cache coherency
Use of individual CPU cores
or CPU core clusters (CC)
in multicore processors
Design aspects affecting the implementation of the intra-processor
interconnect in multicore processors
Implementing intra-processor interconnects off-die, on-die or even both off-die and on-die
Not discussed

## Slide 14: 2.1 Overview of intra-processor interconnects (4)
Use of individual CPU cores or CPU core clusters (CC) in multicore
processors
Use of single CPU cores
Use of CPU core clusters (CC)
Use of individual CPU cores or CPU core clusters (CC) in multicore processors
Single-level interconnects
for the CPU cores
Single or two-level interconnects
for the CPU cores

## Slide 15: 2.1 Overview of intra-processor interconnects (5)
Use of single CPU cores or CPU core clusters in multicore processors
Use of single CPU cores
Use of CPU core clusters
Use of single CPU cores or CPU core clusters in multicore processors
ARM11 MPCore (2004)
ARM Cortex-A9 MPCore
as an option (2007)
ARMv7 based processors
as an option (2009-2014)
ARMv8.0 based processors
as default (2012-2016)
AMD’s CCX modules
in Zen processors (2017-)
Intel’s “modules” in
Silvermont and next cores based
Atom processors (2013- 2016)
Intel “tiles” in Silvermont
core based Knights Landing
processors (2015)
Use of core clusters
of 2 CPU cores
Use of core clusters
of 4 CPU cores
Use of core clusters
of 8 CPU cores
ARMv8.2 based processors
as default (2017)
Intel’s typical choice
in multicores except
those indicated here
(2006-)
AMD’s Families 08h,
10h/11h/12h/14h/16h
(2003-2015)
AMD’s “compute modules”
in the Family 15h (Bulldozer)
line (2011-2015)
IBM POWER 4 to 8
(2001-2014)
IBM’s “SMT4/8 core” in the
POWER9 (2017)
ARM
Intel
AMD
IBM

## Slide 16: 2.1 Overview of intra-processor interconnects (6)
Example 1: Use of single CPU cores in Intel’s Core 2 family [25]

## Slide 17: 2.1 Overview of intra-processor interconnects (7)
The Bulldozer “module” does not have two entire cores, it has dedicated FX
components to each core but also shared components for both cores, as seen in the
Figure below.
Example 2: Use of core clusters of dual CPU cores (called modules)
in AMD’s Bulldozer line (from 2011 on) [26]
Figure: The 2-core Bulldozer “module” with dedicated and shared components [26]

## Slide 18
Up to 72 Silvermont (Atom) cores
4 threads/core
2 512 bit Vector Processing Units (VPU)
2D mesh architecture
6 channels DDR4-2400,
up to 384 GB,
8/16 GB high bandwidth on-package
MCDRAM memory, >500 GB/s
36 lanes PCIe 3.0
200 W TDP
3.1 Overview of intra-processor interconnects (8)
Example 3: Use of core clusters of 2 CPU cores (called tiles)
in Intel’s 72-core Knights Landing processor (2015) [27]
Note that the communication Hub and the 1 MB L2
are shared by both cores

## Slide 19: 2.1 Overview of intra-processor interconnects (9)
Early Core Cluster
Advanced Core Cluster
SCU
CPU
core
L1 I/D
CPU
core
L1 I/D
CPU
core
L1 I/D
CPU
core
L1 I/D
L2 $ with SCU
CPU
core
L1 I/D
CPU
core
L1 I/D
CPU
core
L1 I/D
CPU
core
L1 I/D
Example 4: Use of core clusters of 4 cores in ARM’s ARM11 Mpcore
and Cortex-A MPCore processors (from 2004 on)
ARM11 MPCore (2004)
Cortex-A7/A8/A9/A7 MPCore
(L2 $ optional)
(2005-2011)
Cortex-A15/A17 MPCore
(L2 $ mandatory)
(2010/2014)
all ARMv8.0 models
(L2 $ mandatory)
(2012-2016)
To the interconnect
To the interconnect
SCU: Snoop Control Unit

## Slide 20: 2.1 Overview of intra-processor interconnects (10)
Cortex-A73 core
ARMv8.0 CPU
The ARM Cortex-A73 core cluster of up to 4 cores (2015) [28]
Shared units
ACP: Accelerator Coherency Port (an AXI 64-bit slave port which
can be connected to a DMA engine or a non-cached
coherent master (Source: ARM).
SCU: Snoop Control Unit
AMBA 4 AXI4/ACE: Interface

## Slide 21: 2.1 Overview of intra-processor interconnects (11)
Note
ARM’s core clusters will be included (one or more) into the application processors
of smartphones or tablets.

## Slide 22: 2.1 Overview of intra-processor interconnects (12)
2x
16 bit
2x
16 bit
Example for including two core clusters into an application processor
(Samsung's Exynos 7 Octa 7420 processor with two ARM core clusters) [29]

## Slide 23: 2.1 Overview of intra-processor interconnects (13)
Example 5: ARM’s DynamIQ Core Cluster of up to 8 cores (2017)
Early Core Cluster
(Up to 4 cores)
Advanced Core Cluster
(Up to 4 cores)
DynamIQ Core Cluster
(Up to 8 cores)
CPU1
core
L1 I/D
L2 $
CPU1
core
L1 I/D
L2 $
CPU2
core
L1 I/D
L2 $
CPU2
core
L1 I/D
L2 $
..
..
L3 $ with SCU
SCU
CPU
core
L1 I/D
CPU
core
L1 I/D
CPU
core
L1 I/D
CPU
core
L1 I/D
L2 $ with SCU
CPU
core
L1 I/D
CPU
core
L1 I/D
CPU
core
L1 I/D
CPU
core
L1 I/D
ARM11 MPCore (2004)
Cortex-A7/A8/A9/A7 MPCore
(L2 $ optional)
(2005/2007/2011)
Cortex-A15/A17 MPCore
(L2 $ mandatory)
(2010/2014)
all ARMv8.0 models
(L2 $ mandatory)
(2012-2016)
Cortex-A55/7A5/A76
(2017/2017/2018)
To the interconnect
To the interconnect
To the interconnect

## Slide 24: 2.1 Overview of intra-processor interconnects (14)
ARMv8.2 support, (Cortex-A55/75/76)
2 CPU types, up to 8 cores but up to 4 b core/cluster
Private L2 caches, shared L3 cache
ARMv8.0 support, e.g. Cortex-A53/
A57/A72/A73, up to 4 cores/cluster
Shared L2 cache
Cortex-A73 core
ARMv8.0 CPU
big.LITTLE Core Cluster (2015) [28]
DynamIQ Core Cluster (2017) [30]
*
Contrasting the 8-core DynamIQ Core Cluster vs.the previous 4-core cluster

## Slide 25: 2.1 Overview of intra-processor interconnects (15)
Support of cache coherency in intra-processor interconnects
Non cache-coherent
interconnects
Cache coherent
interconnects
b) Support of cache coherency in intra-processor interconnects
Note that all recent interconnects support cache coherency.
Maintaining cache coherency is however a complex issue of its own and it
will not be discussed in this Chapter.
Early interconnects
All recent interconnects

## Slide 26: 2.1 Overview of intra-processor interconnects (16)
Off-die or on-die intra-processor interconnects
On-die interconnects
Off-die interconnects
Used to interconnect
functional units of a processor off-die
Used to interconnect
functional units of a processor on-die
P
NB
SB
Per./IO
GPU
Per./IO
M
Per./IO
Ring bus
MC
Per.
---
CC
--
A
IO
--
CC: Core Cluster
MC: Memory Controller
c) Implementing intra-processor interconnects off-die, on-die or even
partly off-die and partly on-die

## Slide 27: 2.1 Overview of intra-processor interconnects (17)
There is also feasible to use partially off-die and partially on-die interconnects.
In this case, e.g. cores, the GPU and L3 cache segments are interconnected in
the processor on-die whereas other agents, like I/O off-die, as discussed in
Section 2.3.4.
Note

## Slide 28
2.2 Off-die intra-processor interconnects
2.2.1 Overview
2.2.2 Bus-based off-die interconnects
2.2.3 Chipset-based off-die interconnects

## Slide 29
2.2.1 Overview

## Slide 30: 2.2.1 Overview (1)
Bus-based
off-die interconnects
(in the 1980’/1990’s)
E.g. Intel’s early desktop platforms (since 1981)
Transactions on a shared bus.
.
Chipset-based
off-die interconnects
(since about 2000)
P
NB
SB
Per./IO
GPU
Per./IO
M
Per./IO
Transactions on a set of dedicated links.
Multiple transactions at a time.
E.g. Intel’s Pentium 4 or early Core 2-based platforms (2000/2006)
Off-die intra-processor interconnects (discussed)
8088/286/386
Processor
Memory/
Bus controller
Main memory
KBD
FD
Adapter
Monitor
Adapter
WD
Adapter
PP
Adapter
SP
Adapter
ISA
Multi-I/O
card
(DRAM/FPM)
I/O devices
2.2.1 Overview

## Slide 31
2.2.2 Bus-based off-die interconnects

## Slide 32: 2.2.2 Bus-based off-die interconnects (1)
2.2.2 Bus-based off-die interconnects
They are the most straightforward type of interconnects.
They provide transactions on a shared bus.
In early implementations bus based interconnects allowed only single
transactions at a time, advanced implementations allow also overlapped
transactions by introducing split transfers.
Bus-based interconnects were used
in early desktop platforms (in the 1980‘s and 1990’s) and also
as on-die interconnects in early smartphones and tablets (in the second half
of the 1990’s),
as indicated next.

## Slide 33: 2.2.2 Bus-based off-die interconnects (2)
Bus-based off-die interconnects -1
They were the first type of interconnects used, as indicated in the next Figure.
ISA bus-based
Topology of Intel’s desktop interconnects
Hub-based
Simple
w/ATA,
USB
w/AGP, ATA,USB
PCI bus-based
8088/80286/ 80386- based PCs
486 and early
Pentium based PCs
Mature Pentium based PCs
Early PII
and PIII
based PCs
Mature
PIII/P4
based PCs
Intel 420
chipsets
Mature Intel 430
chipsets
Intel 440XX
chipsets
Intel 8xx
chipsets
Evolution
Early
implem.
Next implem.
P4 Prescott
based PCs
Intel 915xx
chipsets

## Slide 34: 2.2.2 Bus-based off-die interconnects (3)
ISA: Industry Standard Association
Used typically in 8088/80286/80386-based PCs (since 1981 in IBM PCs)
8088/80286/80386
Processor
Memory/
Bus controller
Main memory
KBD
FD
Adapter
Monitor
Adapter
WD
Adapter
PP
Adapter
SP
Adapter
ISA
Multi-I/O card
(DRAM/FPM)
I/O devices
Example: ISA bus-based platform topology

## Slide 35: 2.2.2 Bus-based off-die interconnects (4)
Historical remark: Evolution of bus based interconnects to hub-based interconnects
in Intel’s desktop platforms
ISA bus-based platforms evolved to hub based platforms in a few steps while
the 8/16 bit wide ISA bus was substituted by the higher performance 32 bit
PCI bus,
PCI bus based chipsets emerged and
step by step more and more I/O devices became attached to the chipset
components rather than to the PCI bus, in other words the chipset took
step by step over the role of the PCI bus.
Intel pursued this evolution by introducing and enhancing their 4xx chipset
family and then replacing their PCI bus-based 4xx chipset family by the
already hub based 8xx chipset family.
In this respect the 4xx chipset family can be considered as a forrunner of the
recent hub-based chipsets.
In connection with this move Intel also renamed the System controller of their
early platforms to MCH (Memory Controller Hub, dubbed also as the North
Bridge) and the I/O Controller to IOH (I/O Controller Hub, named also as the
South Bridge).
The subsequent series of Figures indicates main steps of this evolution.
Note that the word hub originally means the central part of a wheel or in figurative
sense the central part of something.

## Slide 36: 2.2.2 Bus-based off-die interconnects (5)
Used typically in 486 and early Pentium-based PCs along with Intel 420 and early 430 chipsets (1989)
486
System
controller
PCI bus
(Legacy and/or
Processor bus
L2 cache
Main memory
(FPM/EDO)
Peripheral
controller
PCI device
adapter
ISA device
adapter
ISA bus
slow devices)
a) Early PCI bus-based platform with Intel 420 chipset
82425EX
82426EX

## Slide 37: 2.2.2 Bus-based off-die interconnects (6)
Used typically in mature Pentium-based PCs with mature Intel 430 chipsets (~1995)
IDE port: First on the 430FX (Triton, 1995)
ATA/33: First on the 430TX (1997)
USB: First on the 430VX (Triton III, 1996)
Pentium
System
controller
PCI bus
(Legacy and/or
Processor bus
L2 cache
Main memory
(FPM/EDO/SDRAM)
Peripheral
controller
PCI device
adapter
ISA device
adapter
ISA bus
slow devices)
USB
IDE/(ATA/33)
82430
PIIX
PIIX: PCI ISA IDE XCELERATOR
PCI-based platform with IDE/ATA and USB ports with Intel’s 430 chipsets

## Slide 38: 2.2.2 Bus-based off-die interconnects (7)
Used typically in Pentium II and early Pentium III-based PCs with Intel 440xx chipsets (~1998/1999)
System
controller
PCI bus
Processor bus
Main memory
(EDO/SDRAM)
Peripheral
controller
PCI device
adapter
ISA device
adapter
ISA bus
Pentium II/
Pentium III
AGP
2xIDE/ATA33/66
2xUSB
(Legacy and/or
slow devices)
Pentium II has an in-package integrated L2,
Pentium III has on-die integrated L2
82440
PIIX4
c) PCI-based platform with AGP, IDE/ATA and USB ports and Intel’s 440
chipset

## Slide 39: 2.2.2 Bus-based off-die interconnects (8)
Used typically in Pentium 4-based systems with Intel 845 chipsets (~2000)
MCH
PCI bus
Processor bus
Main memory
(DDR/DDR2
ICH
PCI device
adapter
ISA device
adapter
ISA bus
Pentium 4
(Willamette)
AGP
2xIDE/
2x/4x USB
Hub interface
ATA 33/66/100
PCI to ISA
bridge
LPC
Super I/O (KBD, MS, FD, SP, PP, IR)
AC'97
(Legacy and/or
slow devices)
d) Early hub-based platform with Intel’s 845 chipset
82845
ICH2-5
System controller renamed to
MCH (Memory Controller Hub)
(called also as North Bridge)
Peripheral Controller to
ICH (I/O Controller Hub)
(called also as South Bridge)

## Slide 40: 2.2.2 Bus-based off-die interconnects (9)
e) Advanced hub-based system architecture with Intel 915xx chipset and
replacing the parallel PCI bus by the serial PCIe bus
MCH
PCI bus
Processor bus
Main memory
(DDR/DDR2)
IOH
PCI device
adapter
Pentium 4
(Prescott)
PCI E.x16
1xIDE/
8x USB
Hub interface
ATA 33/66/100
LPC (KBD, MS, FD, SP, PP, IR)
AC'97
4x SATA
PCI E.x1 (1x/2x)
LAN 10/100
HDAI
829xx
ICH6/7
Used typically in Pentium 4 (Prescott)-based platforms with Intel’s 9xx chipsets (2004)

## Slide 41: 2.2.2 Bus-based off-die interconnects (10)
Chipset-based off-die interconnects -1
Chipsets provide a set of dedicated point-to-point interconnections.
They allow multiple transactions at a time on different point-to-point paths.

## Slide 42
2.2.3 Chipset-based off-die interconnects

## Slide 43: 2.2.3 Chipset-based off-die interconnects (1)
Discrete
graphics
Integrated
graphics
or
dGPU
Displ.
P
NB
w/GPU
SB
Per./
IO
Per./
IO.
M
Per./
IO
--
--
PCIe
Example of a chipset-based interconnect
(actually of a Core 2 based desktop interconnect providing integrated graphics)
Core 2 (2006)
Figure: Chipset-based off-die interconnect
2.2.3 Chipset-based off-die interconnects

## Slide 44: 2.2.3 Chipset-based off-die interconnects (2)
Chipset-based off-die interconnects -2
Chipsets are parts of platforms.
Historically, a number of platform categories evolved.
Recently, the most important platform categories are as follows:
Servers
Recent most important platform categories
Tablets
Notebooks
Desktops
HEDs
Smartphones
As far as server/HED/desktop and notebook processor families are concerned
recently Intel’s and AMD’s related families dominate the market.
Further on, typically in each chipset category dominant processor firms have
their specific chipset families, e.g. for the desktop category recently Intel has
its Core 2 based desktop chipset family.
Notable exceptions are recent tablet- and smartphone platforms since these
platforms are usually built around SoC processors and do not need chipsets.

## Slide 45: 2.2.3 Chipset-based off-die interconnects (3)
It is worth discussing the evolution path of this desktop chipset family.
In order to simplify our discussion, however we will focus on the evolution
of the platform topology and do not take into account further issues, like
memory type, memory transfer rate, PCIe type etc.
Chipset-based off-die interconnects -3
While discussing chipset based interconnects we will focus on a single example,
that is on Intel’s Core 2-based desktop platforms, further on we will consider
the platform option that supports integrated graphics.

## Slide 46: 2.2.3 Chipset-based off-die interconnects (4)
Evolution of the topology of Intel’s Core 2-based desktop platforms with
integrated graphics (strongly simplified) -1
Preminilary note
Graphics cards (dGPU) provide display output, as seen e.g. below.
Figure: Example graphics card with 16xPCIe 3.0 input and DP, HDMI, DVI
display outputs (actually NVIDIA’s GTX1050) [31]

## Slide 47: 2.2.3 Chipset-based off-die interconnects (5)
Core 2 (2006)
Penryn (2007)
Examples
Nehalem 1. gen. (2008)
6-core Westmere (Golfstown) (2010)
Discrete
graphics
Integrated
graphics
or
(Specific NB models support integrated graphics
like the one seen above)
(As an exception no NB model supports
integrated graphics)
dGPU
Displ.
P
NB
wGPU
SB
Per./
IO
Per./
IO.
M
Per./
IO
--
--
Memory Controller placed on-die.
PCIe
dGPU
P
NB
SB
Per./
IO
Per./
IO.
M
Per./
IO
--
--
PCIe
Evolution of the topology of Intel’s Core 2-based desktop platforms
with integrated graphics -1
Initial Core-2 based desktop platform.

## Slide 48: 2.2.3 Chipset-based off-die interconnects (6)
2. gen. Nehalem (Lynnfield) (2009)
2-core Westmere (Arrandale)
(with in-package integrated graphics
and a PCH model supporting integrated graphics) (2010)
Sandy Bridge (with on-die integrated graphics and
most PCH models supporting integrated graphics) (2011)
Ivy Bridge with on-die integrated graphics and
all PCH models supporting integrated graphics (2012)
FDI: Flexible Display Interface
DMI: Direct Media Interface (4x PCIe 2.0)
PCH: Periphery Control Hub
Examples
P
PCH
w/GPU
Per./
IO
M
Per./
IO
--
--
dGPU
Displ.
FDI
(not used)
DMI
PCIe
PCH
Per./
IO
M
Per./
IO
--
--
dGPU
Displ.
P
GPU
FDI
DMI
PCIe
(In-package or on-die) integrated graphics,
FDI interconnection needed between display and GPU.
Evolution of the topology of Intel’s Core 2-based desktop platforms
with integrated graphics -2
PCIe interconnection placed on-die.
An extra link (FDI) is provided (but not needed)
as a preparation for (in P) integrated graphics

## Slide 49: 2.2.3 Chipset-based off-die interconnects (7)
Evolution of the topology of Intel’s Core 2-based desktop platforms
with integrated graphics support -3
Haswell-based desktop platform (2013)
Broadwell-based desktop platform (2015)
Examples
Display interconnection placed on-die.
PCH provides still VGA, this is why FDI is needed.
From Skylake-based desktop platform on (2015)
Examples
PCH doesn’t provide any more VGA output,
this is why no FDI interconnection path is needed.
PCH
Per./
IO
Per./
IO
M
Per./
IO
--
--
dGPU
Displ.
P
GPU
PCIe
DMI
PCH
Per./
IO
Per./
IO
M
Per./
IO
--
--
dGPU
Displ.
P
GPU
PCIe
FDI
DMI
VGA

## Slide 50: 2.2.3 Chipset-based off-die interconnects (8)
Contrasting Intel’s recent Core 2-based desktop platforms with recent SoC
implementations of mobile platforms
SOC implementation (in-package integration of two dies)
for mobile platforms
Per./
IO
dGPU
M
Displ.
--
--
PCH
Per./
IO
Per./
IO
M
Per./
IO
--
--
dGPU
Displ.
From Haswell-based mobile platforms on (2013)
Examples
P
GPU
P
GPU
PCIe
PCIe
DMI
From Skylake-based desktop platform on (2015)

## Slide 51: 2.2.3 Chipset-based off-die interconnects (9)
Example 1: Core 2-based desktop platform with integrated graphics (2006)
[32]

## Slide 52: 2.2.3 Chipset-based off-die interconnects (10)
Example 2: 1. generation Nehalem-based desktop platform (2008) [33]
(Bloomfield)
No support for integrated graphics
(as it targets high-end desktops with
discrete graphics).

## Slide 53: 2.2.3 Chipset-based off-die interconnects (11)
Example 3: 2. gen. Nehalem-based desktop platform with integrated
graphics (2009) [34]
(Not used)
(Lynnfield)

## Slide 54: 2.2.3 Chipset-based off-die interconnects (12)
Example 4: Sandy Bridge-based desktop platform with integrated graphics
(2011) [35]
FDI: Flexible Display Interface

## Slide 55
Example 5: Haswell-based desktop platform with integrated graphics (2013)
[36]
2.2.3 Chipset-based off-die interconnects (13)
VGA

## Slide 56: 2.2.3 Chipset-based off-die interconnects (14)
Display support of Haswell-based desktop platforms [37]
Intel 8 Series
Chipset

## Slide 57: 2.2.3 Chipset-based off-die interconnects (15)
Remark
Note that Series 7 PCHs already provide 3 digital display ports plus + an analog VGA
port, as seen below.
Figure: Evolution of display support in Ivy Bridge and Haswell based platforms [37]
Intel 8 Series
Chipset Family

## Slide 58: 2.2.3 Chipset-based off-die interconnects (16)
Example 6: (Kaby Lake refresh/Coffee Lake/Cannon Lake)-based desktop
platform with integrated graphics [2017] [38]
No FDI
No VGA

## Slide 59: 2.2.3 Chipset-based off-die interconnects (17)
Example 7: In contrast: Haswell-based notebook platform already became
SoCs (2013) [39]

## Slide 60
2.3 On-die intra-processor interconnects
2.3.1 Introduction to on-die intra-processor interconnects
2.3.2 Bus-based on-die interconnects
2.3.3 Crossbar-based on-die interconnects
2.3.4 Ringbus-based on-die interconnects
2.3.5 2D mesh-based on-die interconnects

## Slide 61
2.3.1 Introduction to on-die intra-processor interconnects

## Slide 62: 2.3.1 Introduction to on-die intra-processor interconnects (1)
Single- or two level implementation
of the on-die interconnect
Key features of on-die intra-processor interconnects (discussed)
Topology of the
on-die interconnect
Single-level
on-die interconnects
Two-level
on-die interconnects
Used typically in processors
built up of single cores
Used typically in processors
built up of core clusters
2.3.1 Introduction to on-die intra-processor interconnects
On-die interconnects were proposed first by researchers of Stanford University
in 2001.

## Slide 63: 2.3.1 Introduction to on-die intra-processor interconnects (2)
Single or two level implementation of the on-die interconnect
Used typically to build a processor or SoC
Examples
Intel's ring interconnect
for 4 cores or more
introduced in the
Sandy Bridge (2011)
Intels 2D-interconnect
e.g. in the 72-core
Knights Landing (2015)
Single-level
on-die interconnects
Two-level
on-die interconnects
ARM's interconnects
a) Single or-two-level implementation of the on-die interconnect

## Slide 64: 2.3.1 Introduction to on-die intra-processor interconnects (3)
Single level on-die inter-processor interconnects
Single- or two level implementation of the on-die interconnect
Used typically within a processor or to build a SoC
Examples
Intel's ring interconnect
for 4 cores or more
introduced in the
Sandy Bridge (2011)
Intels 2D-interconnect
e.g. in the 72-core
Knights Landing (2015)
Single-level
on-die interconnects
Two-level
on-die interconnects
ARM's interconnects
for core clusters:
for the ARM11 MP (2006) and
for the Cortex line
beginning with the
Cortex-A9 (2007)

## Slide 65: 2.3.1 Introduction to on-die intra-processor interconnects (4)
The ring has six bus stops for
interconnecting
The four cores and the
L3 slices share the same
interfaces.
four cores
four L3 slices
the GPU and
the System Agent
System Agent
Example 1 for single level on-die interconnect:
Intel's ring bus for the 4 core Sandy Bridge (2011) [40]

## Slide 66: 2.3.1 Introduction to on-die intra-processor interconnects (5)
Example 2 for single level on-die interconnect:
Intel's dual ring interconnect for the 18-core Haswell-EX (2015) [41]

## Slide 67: 2.3.1 Introduction to on-die intra-processor interconnects (6)
Example 3 for single level on-die interconnect: Intel's 2D-interconnect
in the 72-core Knights Landing (implemented in 36 tiles) (2015) [27]
Up to 72 Silvermont (Atom) cores
in 36 tiles
4 threads/core
2 512 bit vector units
2D mesh architecture
6 channels DDR4-2400,
up to 384 GB,
8/16 GB high bandwidth on-package
MCDRAM memory, >500 GB/s
36 lanes PCIe 3.0
200 W TDP

## Slide 68: 2.3.1 Introduction to on-die intra-processor interconnects (7)
Single- or two level implementation of the on-die interconnect
Used typically to build a processor or SoC
Examples
Intel's ring interconnect
for 4 cores or more
introduced in the
Sandy Bridge (2011)
Intels 2D-interconnect
e.g. in the 72-core
Knights Landing (2015)
Single-level
on-die interconnects
Two-level
on-die interconnects
Two-level on-die interconnects
ARM's on-die interconnects are built up of two levels
the first level interconnects a cluster of cores (up to 4 cores)
the second level interconnects core clusters and other system components,
as shown subsequently.
ARM's interconnects
for core clusters (CC)

## Slide 69: 2.3.1 Introduction to on-die intra-processor interconnects (8)
APB
ATB
Interrupts
Example: 1. level interconnect in ARM’s 4-core CC of Cortex-A72 (2015) [42]
Source: ARM
CC: Core Cluster

## Slide 70: 2.3.1 Introduction to on-die intra-processor interconnects (9)
ARM's 2. level interconnect in the Juno development platform [43]
CCI: Cache Coherent Interconnect

## Slide 71: 2.3.1 Introduction to on-die intra-processor interconnects (10)
Internal architecture
of the CCI-400
cache-coherent
Interconnect [44]

## Slide 72: 2.3.1 Introduction to on-die intra-processor interconnects (11)
On-die implementation of the CCI-400 in the ARM's Juno development platform [45]

## Slide 73: 2.3.1 Introduction to on-die intra-processor interconnects (12)
b) Topology of on-die interconnects
Crossbar-based
Shared bus based
Ring bus-based
Topology of on-die interconnects
2D-mesh-based

## Slide 74: 2.3.1 Introduction to on-die intra-processor interconnects (13)
Shared bus
based interconnects
Crossbar-based
interconnects
AHB based SoCs
(non CC, ~2001) [8]
Topology of on-die interconnects
PL-300 interconnect
(non CC, on AXI3, 2004)
through the CCI 550 interconnect
(CC, on ACE, 2015)
Examples
Intel
ARM
Nehalem (CC, on QPI, 2008)
Evolution of the topology of on-die interconnects -1
CC: Cache Coherent
P
GPU
M
Per./IO
---
---
Bus
Crossbar
M
Per.
Core
GPU
--
--
Higher
performance
for higher nc

## Slide 75: 2.3.1 Introduction to on-die intra-processor interconnects (14)
Topology of on-die interconnects
Ring bus-based
interconnect topology
Ring
MC
Per.
---
CC
--
A
IO
--
2D mesh-based
interconnect topology
CMN-6xx Interconnect for servers
(CC, on CHI, 2017)
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
CC
CC
CC
CC
A
A
CC
CC
A
MC
MC
MC
MC
R
R
R
R
R
A
A
A
MC
MC
IO
IO
IO
IO
IO
IO
P
P
P
P
P
P
Evolution of the topology of on-die interconnects -2
*
CC: Core Cluster
A: Accelerator (e.g. GPU, NPU)
nc: Core count
CCN-5xx interconnect for servers
(CC, on CHI, 2012)
Examples
Intel
ARM
Skylake-SP for servers
(CC, UPI, 2017)
Knights Landing for AI, (2016)
Sandy Bridge (CC, on QPI, 2011)
Less cost
for higher nc
Shorter
access time
for higher nc

## Slide 76
2.3.2 Bus-based on-die interconnects

## Slide 77: 2.3.2 Bus-based on-die interconnects (1)
2.3.2 Bus-based on-die interconnects
They are the most straightforward type of on-die interconnects.
They provide transactions on a shared bus.
Early implementations of bus-based interconnects allowed only single
transactions at a time, more advanced implementations allow also
overlapped transactions by introducing split transfers.
Bus-based on-die interconnects were typically used
in early smartphones and tablets (in the second half of the 1990’s)
in single core devices,
as indicated next in Examples 1 and 2.
Remark
Astonishingly enough, also IBM’s more recent POWER8 server processor makes use
of a bus based on-die interconnect as a related patent shows (see Example 3).

## Slide 78: 2.3.2 Bus-based on-die interconnects (2)
Introduction to the AMBA interconnect open standard family [46]
The AMBA (Advanced Microcontroller Bus Architecture) standard was originally
intended to be as a bus-based interconnect standard for microcontrollers,
as its name indicates but it became the de facto standard for interconnecting
functional blocks in SOC (System-On-a-Chip) designs for smartphones and
tablets.
AMBA is a royalty-free open-standard.
It was originally published about 1996 and went through a number or major
enhancements, designated as AMBA revisions 1 to 5 (up to date), as shown
in the subsequent Figure.
Roughly speaking
Example 1: ARM’s AMBA1 and AMBA2 bus-based interconnect standards
(except the ML AHB bus (Multilevel AHB bus)-based interconnects)
AMBA’s first two revisions (AMBA1 and AMBA2) supported bus-based
interconnects,
the next two revisions (AMBA 3 and AMBA 4) crossbar-based interconnects,
whereas
the subsequent design (AMBA5) already ring bus-based interconnects,
as indicated more detailed in the next Figure.

## Slide 79: 2.3.2 Bus-based on-die interconnects (3)
Support of different interconnect topologies by the AMBA interconnect
standard family [47]
Coherent Hub Inteface
AMBA Coherency Extensions Protocol
Advanced eXtensible Interface
AMBA High Performance Bus
Advanced Peripheral Bus
1995
2000
2010
APB™
ASB™
(1996)
AHB™
AHB-Lite
APB2
APB v1.0
APB v2.0
AXI4-Stream
AXI3
AXI4
AXI4-Lite
ACE™
ACE-Lite
CHI
AMBA1
(5/1999)
AMBA2
(6/2003)
AMBA3
(3/2010)
AMBA4
(6/2013)
AMBA5
(ARM7/9)
(ARM11, Cortex-A9)
(Cortex-A15/A7 ARM big.LITTLE)
(Cortex A57/A53)
(10/2011)
Advanced System Bus
Advanced Trace Bus
ATB
ATB v2.0
(3/2012)
(9/2004)
(5/1999)
≈
ML AHB
Multi-layer AHB
ATB v1.0
(6/2006)
Used in
Revision
(3/2001)
(3/2001)
Bus-based InCn
Crossbar-based
(not CC) InCn
Crossbar-based
(CC InCn)
Ring-bus-based
(CC InCn)
CC: Cache Coherent
InCn: Interconnect
Bus based interconnects

## Slide 80: 2.3.2 Bus-based on-die interconnects (4)
A typical AMBA1 system [48]
ASB
APB

## Slide 81: 2.3.2 Bus-based on-die interconnects (5)
a) The ASB bus is a high performance parallel bus, more precisely a high performance
bus IP utilizable for SOC designers.
multiple masters,
burst transfers and
pipelining in two stages (as bus granting and bus transfers may be performed
in parallel).
Nevertheless, there is a limitation of the ASB bus as only a single master
might be active at a time.
c) The interface signals include
mostly uni-directional lines, like the address, control or transfer response lines,
but the data lines carrying write and read data between the masters and the
slaves are bi-directional.
In addition the data line of the APB bus is also bi-directional.
d) The ASB protocol makes use of both edges of the clock signal.
Main features of the ASB bus [48]
b) Bus operation supports

## Slide 82: 2.3.2 Bus-based on-die interconnects (6)
The APB bus (Advanced Peripheral Bus) -1 [48]
It appears as a local secondary bus encapsulated as a single slave device,
as indicated below.
Figure: A typical AMBA system [48]
ASB
APB

## Slide 83: 2.3.2 Bus-based on-die interconnects (7)
Main features of the APB bus [48]
The APB bus is a simple, low-power extension to the system bus which builds on
ASB signals directly.
It does not support pipelining.

## Slide 84: 2.3.2 Bus-based on-die interconnects (8)
Remark
The AMBA2 standard is an enhancement of the AMBA1 in order to
increase performance, e.g. by supporting split transactions for allowing
in-parallel transfers and
allow a more straightforward implementation, e.g. by using only
uni-directional signals (also for data buses, in contrast to the ASB protocol).

## Slide 85: 2.3.2 Bus-based on-die interconnects (9)
Main enhancements of the AHB bus vs. the ASB bus [49]
a) Spit transactions.
This allows enhanced pipelining on the bus by overlapping the address and
data phases of transactions from different bus masters.
b) Enhanced burst transactions.
c) Wider data bus options (termed as transfer size alternatives).
d) Using only uni-directional signals (also for data buses, in contrast to the ASB
protocol).
e) Using only the rising edge of the bus clock (in contrast to the ASB protocol where
both edges are used).
The AHB bus

## Slide 86: 2.3.2 Bus-based on-die interconnects (10)
Example 2: Intel’s PXA27x used originally in the Blackberry Pearl 8100 [50]

## Slide 87: 2.3.2 Bus-based on-die interconnects (11)
Example 3: IBM’s POWER8 server bus (2014) -1
The POWER8 has 12 cores arranged on the die as indicated below.
Figure: Layout of the POWER8 die [51]

## Slide 88: 2.3.2 Bus-based on-die interconnects (12)
Example 3: IBM’s POWER8 server bus (2014) -2
In IBM’s technical documentation no details could be found about the on-die bus,
nevertheless an IBM patent [52] reveals the following details:

## Slide 89: 2.3.2 Bus-based on-die interconnects (13)
According to this patent IBM made use of a complex bus consisting of trunk
segments, that acts as a path through for the signals, and interconnects
horizontally the neighboring trunk segments and
vertically the top and bottom Compute Element (core and L3 cache segment)
Figure: Trunk segment of the POWER8 bus [52]
To the top Compute Element
To the bottom Compute Element
PRESP Partial Response
CREPS Combined Response
with a given trunk segment.
Example 3: IBM’s POWER8 server bus (2014) -3

## Slide 90: 2.3.2 Bus-based on-die interconnects (14)
Note that the POWER8 makes use of a very complex bus, that transfers
horizontally 1165 bits and
vertically 575 bits.
Example 3: IBM’s POWER8 server bus (2014) -4

## Slide 91
2.3.3 Crossbar-based on-die interconnects

## Slide 92: 2.3.3 Crossbar-based on-die interconnects (1)
2.3.3 Crossbar-based on-die interconnects
They provide point-to-point connections from a number of sources to a number of
sinks via appropriated links by means of a crossbar switch (interconnect matrix),
as indicated in the Figure below (for better clarity we show only one direction). [53]

## Slide 93: 2.3.3 Crossbar-based on-die interconnects (2)
Support of cache coherency
Non cache coherent
interconnects
Cache coherent
interconnects
Support of cache coherency in crossbar-based interconnects
Early, straightforward implementations
Advanced implementations
Cache coherency is maintained by software.
Induces higher coherency traffic.
Is less effective in terms of
performance and power consumption.
Cache coherency is maintained by hardware.
Induces less coherency traffic.
Is more effective in terms of
performance and power consumption
Examples
PL-300 (2004)
NIC-301 (2006)
NIC-400 (2010)
CCI-400 (2010)
CCI-500 (2014)
CCI-550 (2015)
ARM
Intel
Nehalem (2008)

## Slide 94: 2.3.3 Crossbar-based on-die interconnects (3)
Multi-layer AHB
Overview
DVI 0045A
ARM Limited. 2001
It can be built up by buses as well as multiplexers and demultiplexers, as shown in
the Figure below (only for the Master to Slave direction [54].
Implementation of the crossbar switch
Figure: Implementation of the crossbar switch in the Master to Slave direction [54]

## Slide 95: 2.3.3 Crossbar-based on-die interconnects (4)
Example 1: Five-way crossbar switch in Intel’s Nehalem based Xeon 5500
processor (2010)
(Crossbar)

## Slide 96: 2.3.3 Crossbar-based on-die interconnects (5)
Example 2: Internal structure of ARM’s NIC-400 crossbar-based,
non cache coherent interconnect with AXI4 links (2010) [55]
NIC: Network Interconnect

## Slide 97: 2.3.3 Crossbar-based on-die interconnects (6)
ARM’s bus standards underlying their non cache coherent crossbar-based
on-die interconnects
Coherent Hub Inteface
AMBA Coherency Extensions Protocol
Advanced eXtensible Interface
AMBA High Performance Bus
Advanced Peripheral Bus
1995
2000
2010
APB™
ASB™
(1996)
AHB™
AHB-Lite
APB2
APB v1.0
APB v2.0
AXI4-Stream
AXI3
AXI4
AXI4-Lite
ACE™
ACE-Lite
CHI
AMBA1
(5/1999)
AMBA2
(6/2003)
AMBA3
(3/2010)
AMBA4
(6/2013)
AMBA5
(ARM7/9)
(ARM11, Cortex-A9)
(Cortex-A15/A7 ARM big.LITTLE)
(Cortex A57/A53)
(10/2011)
Advanced System Bus
Advanced Trace Bus
ATB
ATB v2.0
(3/2012)
(9/2004)
(5/1999)
≈
ML AHB
Multi-layer AHB
ATB v1.0
(6/2006)
Used in
Revision
(3/2001)
(3/2001)
Bus-based InCn
Crossbar-based
(not CC) InCn
Crossbar-based
(CC InCn)
Ring-bus
or 2D mesh-based
(CC InCn)
CC: Cache Coherent
InCn: Interconnect
Non cache coherent
crossbar-based

## Slide 98: 2.3.3 Crossbar-based on-die interconnects (7)
NIC-400 based entry-level smartphone platform [56]

## Slide 99: 2.3.3 Crossbar-based on-die interconnects (8)
Example 3: ARM’s cache coherent, crossbar based CCI-400 interconnect
with ACE links (2011) [57]
.
Remark
Interface ports receiving data requests e.g. from processor cores, the GPU, DMAs
or the LCD, are called Slaves whereas those initiating data requests e.g. to the
memory or other peripherals are designated as Masters, as indicated in the Figure
above.
CCI: Cache Coherent Interconnect

## Slide 100: 2.3.3 Crossbar-based on-die interconnects (9)
ARM’s bus standards underlying their cache coherent, crossbar-based
on-die interconnects
Coherent Hub Inteface
AMBA Coherency Extensions Protocol
Advanced eXtensible Interface
AMBA High Performance Bus
Advanced Peripheral Bus
1995
2000
2010
APB™
ASB™
(1996)
AHB™
AHB-Lite
APB2
APB v1.0
APB v2.0
AXI4-Stream
AXI3
AXI4
AXI4-Lite
ACE™
ACE-Lite
CHI
AMBA1
(5/1999)
AMBA2
(6/2003)
AMBA3
(3/2010)
AMBA4
(6/2013)
AMBA5
(ARM7/9)
(ARM11, Cortex-A9)
(Cortex-A15/A7 ARM big.LITTLE)
(Cortex A57/A53)
(10/2011)
Advanced System Bus
Advanced Trace Bus
ATB
ATB v2.0
(3/2012)
(9/2004)
(5/1999)
≈
ML AHB
Multi-layer AHB
ATB v1.0
(6/2006)
Used in
Revision
(3/2001)
(3/2001)
Bus-based InCn
Crossbar-based
(not CC) InCn
Crossbar-based
(CC InCn)
Ring-bus or
2D mesh-based
(CC InCn)
CC: Cache Coherent
InCn: Interconnect
Cache coherent
crossbar-based

## Slide 101: 2.3.3 Crossbar-based on-die interconnects (10)
Smartphone platform based on the cache coherent CCI-400 interconnect [47]
(Generic Interrupt Controller)
(GPU)
(Network Interconnect)
(Memory
Management Unit)
(Dynamic Memory Controller)
(DVM: Distributed
Virtual Memory)

## Slide 102
2.3.4 Ringbus-based on-die interconnects

## Slide 103: 2.3.4 Ringbus-based on-die interconnects (1)
Crossbar-based
interconnect topology
[from 2004 on]
ARM's interconnects
for mobiles
PL-300 (2004)
CCI-400 (2011)
Cross bar
MC
Per.
CC
A
IO
Ringbus-based
interconnect topology
[from 2012 on]
ARM's interconnects
for servers
CCN-504 (2012)
CCN-508 (2013)
Ring
MC
Per.
---
CC
--
A
IO
--
2.3.4 Ring bus-based on-die interconnects
For higher core counts or higher number of data sources and sinks (like cores (CC),
accelerators (A), I/O links etc.) the implementation cost of on-die crossbar-based
interconnects raises quadratic and a ring bus-based interconnect becomes more
attractive, as indicated below.
--
--
Examples
--
Less cost
for higher nc
nc: Core count

## Slide 104: 2.3.4 Ringbus-based on-die interconnects (2)
2006
2008
2010
2012
2014
Year
IBM/Toshiba/Sony
Cell
(8C)
Graphics/HPC
Intel
Larrabee
(16C-24C)
Graphics/HPC)
Westmere-EX
(10C)
Servers
and subsequent
server processors
Sandy Bridge
(!C+GPU
DT/mobiles
and subsequent
processors
Xeon Phi
Knights Ferry
(32C)
HPC
Xeon Phi
Knights Corner
(~60C)
HPC
ARM
CCN-504
CCN-508
CCN-502
CCN-512
Emergence of ring-bus based on-die interconnects

## Slide 105: 2.3.4 Ringbus-based on-die interconnects (3)
The ring has six bus stops for
interconnecting
The four cores and the
L3 slices share the same
interfaces.
four cores
four L3 slices
the GPU and
the System Agent
System Agent
Example 1: The ring bus of Intel’s 4-core Sandy Bridge (2011) [40]

## Slide 106: 2.3.4 Ringbus-based on-die interconnects (4)
Example 2: Dual ring buses of Intel's 18-core Haswell-EX (2015) [41]

## Slide 107: 2.3.4 Ringbus-based on-die interconnects (5)
Example 3: Ring interconnect of Intel’s 57-61 core Xeon Phi
Knights Corner (2012) [58]

## Slide 108: 2.3.4 Ringbus-based on-die interconnects (6)
Example 4: The ring bus of ARM’s CCN-504 (dubbed Dickens)
cache coherent interconnect [59]
Remark: The Figure indicates only 15 ACE-Lite slave ports and 1 master port
whereas ARM's specifications show 18 ACE-Lite slave ports and 2 master ports.

## Slide 109: 2.3.4 Ringbus-based on-die interconnects (7)
ARM’s bus standards underlying their cache coherent, ringbus-based
on-die interconnects
Coherent Hub Inteface
AMBA Coherency Extensions Protocol
Advanced eXtensible Interface
AMBA High Performance Bus
Advanced Peripheral Bus
1995
2000
2010
APB™
ASB™
(1996)
AHB™
AHB-Lite
APB2
APB v1.0
APB v2.0
AXI4-Stream
AXI3
AXI4
AXI4-Lite
ACE™
ACE-Lite
CHI
AMBA1
(5/1999)
AMBA2
(6/2003)
AMBA3
(3/2010)
AMBA4
(6/2013)
AMBA5
(ARM7/9)
(ARM11, Cortex-A9)
(Cortex-A15/A7 ARM big.LITTLE)
(Cortex A57/A53)
(10/2011)
Advanced System Bus
Advanced Trace Bus
ATB
ATB v2.0
(3/2012)
(9/2004)
(5/1999)
≈
ML AHB
Multi-layer AHB
ATB v1.0
(6/2006)
Used in
Revision
(3/2001)
(3/2001)
Bus-based InCn
Crossbar-based
(not CC) InCn
Crossbar-based
(CC InCn)
Ring-bus or
2D mesh-based
(CC InCn)
CC: Cache Coherent
InCn: Interconnect
Cache coherent
ringbus or 2D mesh-based

## Slide 110: 2.3.4 Ringbus-based on-die interconnects (8)
Mobile platform based on the cache-coherent CCN-504 interconnect [60]

## Slide 111
2.3.5 2D mesh-based on-die interconnects

## Slide 112: 2.3.5 2D mesh-based on-die interconnects (1)
Ring interconnects cause high core-to-core transfer times for large core counts, e.g.
for 24-cores, as indicated in the Figure below [25]
Ring-bus of Intel’s
24-core Broadwell-EX
server processor [25]
2.3.5 2D mesh-based on-die interconnects -1

## Slide 113: 2.3.5 2D mesh-based on-die interconnects (2)
Ring
interconnect
Mesh
interconnect
*
2D mesh-based on-die interconnects -2
Long core-to-core transfer times may limit performance, as seen in the Figure
below for ARM’s interconnects [61], this motivated the introduction of 2D mesh
interconnects.

## Slide 114: 2.3.5 2D mesh-based on-die interconnects (3)
Ringbus-based
interconnect topology
[from 2012 on]
ARM's interconnects
for servers
CCN-500
Ring
MC
Per.
---
CC
--
A
IO
--
2D mesh-based
interconnect topology
[from 2016 on]
ARM's interconnects
for servers
CMN-600
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
CC
CC
CC
CC
A
A
CC
CC
A
MC
MC
MC
MC
R
R
R
R
R
A
A
A
MC
MC
IO
IO
IO
IO
IO
IO
P
P
P
P
P
P
*
Move from ringbus-based interconnects to 2D mesh-based interconnects -1
Higher performance
for high core counts

## Slide 115
2.3.5 2D mesh-based on-die interconnects (4)
Interconnection style of many and multi-core processors
Ring architecture
Mesh (2D grid) architecture
Sony/Toshiba/IBM Cell (2006): 8 cores
Tile processor (2007): 80 cores
SCC (2010): 48 cores
Larrabee (2009). 24-32 cores (cancelled)
Xeon Phi
Knights Ferry (2010): 32 cores
Knights Corner (2012): 57-61 cores
Xeon Phi
Knights Landing (2016): up to 72 cores
Nehalem-EX (Beckton) (2010) up to 8 cores
All Sandy Bridge lines (2011) up to 8 cores
All Ivy Bridge lines (from 2012 on) up to 15 cores
to
All Broadwell lines (from 2014 on) up to 24 cores
Skylake (2015) up to 4 cores
Skylake-X (HED) (2017) up to 18 cores
Skylake-SP (2017) up to 28 cores
Intel
(ARM CCN504 (2012) to CCN512 (2014) Interconnect
IBM
POWER9 (2017)
CMN6xx (2016) Interconnect)
Move from ringbus-based interconnects to 2D mesh-based interconnects -2

## Slide 116
Example 1: 2D mesh in Intel’s 72-core Knights Landing processor (2016) [27]
Up to 72 Silvermont (Atom) cores
4 threads/core
2 512 bit vector units
2D mesh architecture
6 channels DDR4-2400,
up to 384 GB,
8/16 GB high bandwidth on-package
MCDRAM memory, >500 GB/s
36 lanes PCIe 3.0
200 W TDP
2.3.5 2D mesh-based on-die interconnects (5)

## Slide 117: 2.3.5 2D mesh-based on-die interconnects (6)
Example 2: 2D mesh in Intel’s up to 28-core Xeon Skylake-SP (2017) [62]

## Slide 118: 2.3.5 2D mesh-based on-die interconnects (7)
Example 3: 2D mesh in ARM’s CMN-6xx cache coherent interconnect (2016)
[63]

## Slide 119: 2.3.5 2D mesh-based on-die interconnects (8)
Use of ARM’s 2D mesh interconnect (CMN-600) to build a server [64]
*
10711syste

## Slide 120: 2.3.5 2D mesh-based on-die interconnects (9)
Power consumption of on-die interconnects
We note that 2D interconnects have considerable more power consumption than
ring bus interconnects, as the next example shows.

## Slide 121: 2.3.5 2D mesh-based on-die interconnects (10)
Example 1: Layout of Intel’s 6-core Coffee Lake 8700K using a ring bus [77]

## Slide 122: 2.3.5 2D mesh-based on-die interconnects (11)
Breakdown of power consumption between the cores and the IF in Intel’s
6-core Coffee Lake 8700K processor using a ring bus [73]

## Slide 123: 2.3.5 2D mesh-based on-die interconnects (12)
Example 2: Layout of a 4x4 2D mesh [73]

## Slide 124: 2.3.5 2D mesh-based on-die interconnects (13)
Breakdown of power consumption between the cores and the IF in Intel’s
18-core Skylake X 7980XE processor using a 2D mesh [73]
Note that the 2D mesh of the 7980X differs from that shown before.

## Slide 125
2.4 Use of both off-die and on-die interconnects

## Slide 126: 2.4 Use of both off-die and on-die interconnects (1)
2.4 Use of both off-die and on-die interconnects
Multicores imply a new requirement, that is to provide core-to-to communication,
in other words to allow interactions, like synchronization or data exchange
between cores.
In case of on-die intra-processor interconnects this requirement needs to
taken into consideration by default.
Nevertheless, off-die interconnects need to be augmented for multicores
appropriately by an on-die interconnect.
Subsequently, we show two examples for this.

## Slide 127: 2.4 Use of both off-die and on-die interconnects (2)
2. gen. Nehalem (Lynnfield) (2009)
P
PCH
w/GPU
Per./
IO
M
Per./
IO
--
--
dGPU
Displ.
FDI
(not used)
DMI
PCIe
PCIe interconnection placed on-die.
An extra link (FDI) is provided
(but not needed) as a preparation
for integrated graphics
Example 1 for using both off-die and crossbar-based on-die interconnect
in Intel’s desktops [40]
(Crossbar)

## Slide 128: 2.4 Use of both off-die and on-die interconnects (3)
2-core Westmere (Arrandale)
(with in-package integrated graphics
and a PCH model supporting integrated graphics) (2010)
Sandy Bridge (with on-die integrated graphics and
a PCH model supporting integrated graphics) (2011)
Ivy Bridge with on-die integrated graphics and
all PCH models supporting integrated graphics (2012)
PCH
Per./
IO
M
Per./
IO
--
--
dGPU
Displ.
P
GPU
FDI
DMI
PCIe
Integrated graphics
(in-package or on-die)
FDI interconnection needed between
display and GPU.
FDI
Example 2 for using both off-die and ring-based on-die interconnect
in Intel’s desktops [40]

## Slide 129
4. Inter-processor interconnects
4.1 Overview of inter-processor interconnects
4.2 One or two level interconnects between sockets
4.3 Inter-processor interconnect topologies
4.4 Layout of the interconnect links

## Slide 130
4.1 Overview of inter-processor interconnects

## Slide 131: 4.1 Overview of inter-processor interconnects (1)
Intra-processor
interconnects
Inter-node
interconnects
Main functional levels of interconnects
Inter-processor
interconnects
Interconnects the functional
units of a processor
P
Per./
IO
GPU
Disp
M
.
Interconnects processors
within a server
(e.g. DP/MP servers) [2]
Interconnects nodes
(e.g. 2P/4P servers) of a processor cluster [3]
4.1 Overview of inter-processor interconnects -1

## Slide 132: 4.1 Overview of inter-processor interconnects (2)
Overview of inter-processor interconnects -2
They interconnect processors of a multiprocessor, as seen e.g. below [2].
Intel’s Entry and Efficient Performance (Romley) platform options
Intel’s Ivy Bridge-based High-end (Brickland) platform options

## Slide 133: 4.1 Overview of inter-processor interconnects (3)
Key aspects of inter-processor interconnects
Partially or fully connected
mesh
One- or two level
processor interconnects
Key aspects of the inter-processor interconnects (discussed)
Layout of the
interconnect links
Section 3.2
Section 3.3
Section 3.4

## Slide 134
3.2 One or two level inter-processor interconnects

## Slide 135: 3.2 One or two level inter-processor interconnects (1)
One-level interconnects
Two-level interconnects
One or two level inter-processor interconnects
Typical use
Intel’s and AMD’s 2S to 8S servers and
IBM’s entry level servers
3.2 One or two level inter-processor interconnects
Processors are interconnected first into nodes,
e.g. into nodes with 4 processors each,
and the nodes are also properly interconnected, e.g. [66]
Processors are directly interconnected, e.g. [65]
(SKL: Skylake-SP Xeon)
IBM’s high-end servers with 16 or more processors

## Slide 136
3.3 Inter-processor interconnect topologies

## Slide 137: 3.3 Inter-processor interconnect topologies (1)
3.3 Inter-processor interconnect topologies
We consider this subject separately for one and two level interconnects.
Inter-processor interconnect topologies
Inter-processor interconnect topologies
of one level interconnects
Inter-processor interconnect topologies
of two level interconnects
Typically used in entry or “effective performance”
oriented server platforms
Typically used in IBM’s high-performance
oriented server platforms

## Slide 138: 3.3 Inter-processor interconnect topologies (2)
Inter-processor interconnect topologies of one-level interconnects
Inter-processor interconnect topologies
of one-level interconnects
Partially connected mesh
Fully connected mesh
Typically used in entry or “efficient performance”
oriented platforms
Typically used in high-performance
oriented platforms
Examples for 4S servers [2]

## Slide 139: 3.3 Inter-processor interconnect topologies (3)
Inter-processor interconnect topologies
of two-level interconnects
1. level inter-processor interconnect topology
of two-level interconnects
2. level inter-processor interconnect topology
of two-level interconnects
Inter-processor interconnect topologies of two-level interconnects

## Slide 140: 3.3 Inter-processor interconnect topologies (4)
1. level inter-processor interconnect topology of two-level interconnects
Typically, IBM’s high level POWER servers make use of two-level inter-processor
interconnect topologies.
Usually, these servers are built up of 4-processor nodes interconnected by a full mesh,
as seen below for IBM’s POWER6 servers.
Figure: IBM POWER6 4-processor server node interconnected by a full mesh (2008)
[66]

## Slide 141: 3.3 Inter-processor interconnect topologies (5)
2. level inter-processor interconnect topology of two-level interconnects
2. level inter-processor interconnect topology
of two-level interconnects (examples)
Ringbus-based interconnect
Fully connected mesh interconnect
Figure: 2. level ringbus-based interconnect
of POWER5 systems (2004) [66]
(There are additional data links to reduce latency)
Figure: 2. level fully connected mesh-based interconnect
of POWER6 systems (~2007) [66]

## Slide 142: 3.3 Inter-processor interconnect topologies (6)
More detailed 2. level interconnect of the POWER6-based POWER 595 [66]
We note that
the four processors of a node
are designated by S, T, U, V.
Each processor has two links,
for inter-node connections,
termed A and B.
Thus each node has 8 links for
node-to-node connections:
SA, SB, TA etc.
Seven of these links are used to
connect a given node to the
seven other nodes in an
8-node system, as indicated
left.
Thus up to two hops are
needed from a given processor
to another (up to one hop
in the source node and up to
another hop in the destination
node).

## Slide 143: 3.3 Inter-processor interconnect topologies (7)
2. Example for second level interconnect in POWER8-based IBM’s E880
systems (2014) [67]
3 X-buses per processor:
Intra-node links
to processors within a node
(called Drawer).
(They provide a
fully connected mesh
between processors
building a node).
3 A-buses per processor: Inter-node links
to processors external to a node
(They provide a fully connected mesh
for any given processor to any given processor
via intra-node links (if needed) and two switches,
(designated by T).

## Slide 144
3.4 Layout of the interconnect links

## Slide 145: 3.4 Layout of the interconnect links (1)
3.4 Layout of the interconnect links
Clearly, links of recent interconnects have to support cache coherency of the
entire platform.
Vital interconnect links used in multicore multi-socket servers:
Vendor | Server family | Interconnect link
Intel | Xeon (from Nehalem to Broadwell) | QPI (Quick Path Interconnect)
Intel | Xeon Skylake-SL | UPI (Ultra Path Interconnect
AMD | Opteron | HT (HyperTransport)
IBM | POWER7/8 | Not disclosed (except in patents)

## Slide 146: 3.4 Layout of the interconnect links (2)
Key features: Layered protocol
Key features of the physical layer: Unidirectional point-to-point links,
2-Byte data width, DDR data rate, differential signaling
Evolution of the QPI bus
QPI | Base clock | Platforms | Data rate (up to) (in each dir.) | Year
QPI | 3.2 GHz | Nehalem (server/desktop) | 12.8 GB/s | 2008
QPI 1.1 | 4.0 GHz | Sandy Bridge EN/EP Ivy Bridge-EN/EP/EX Westmere EN/EP/EX | 16.0 GB/s | 2010-14
QPI 1.1 | 4.8 GHz | Haswell EN/EP/EX Broadwell EN/EP/EX | 19.2 GB/s | 2014-16
UPI | Base clock | Platforms | Data rate (up to) (in each dir.) | Year
UPI | 5.2 GHz | Skylake-SP | 20.8 GB/s | 2017
Example 1: Intel’s QPI bus (Quick Path Interconnect bus)
Replacing the QPI bus by the UPI (Ultra Path Interconnect) bus)

## Slide 147: 3.4 Layout of the interconnect links (3)
QPI’s layered communication protocol and main tasks of the layers [68]
ibm powernik

## Slide 148
16 data
2 protocol
2 CRC
TX Unidirectional link
RX Unidirectional link
Physical layer of the QPI bus [69]
(DDR data transfer)
3.4 Layout of the interconnect links (4)

## Slide 149: 3.4 Layout of the interconnect links (5)
Packets
Flits
Phits
Transfer entities of the QPI protocol [68]
Messages)
A Phit contains all bits transferred by the Physical layer on a single clock edge,
that is 20 bits for a full width (20 lanes), 10 bits for a half width and 5 bits
for a quarter width link implementation).
A Flit is always 80 bits long regardless of the link width, so the number of
Phits needed to transmit a Flit will varies on the link width.

## Slide 150: 3.4 Layout of the interconnect links (6)
A 80-bit long Flit of Intel’s QPI [70]
A Flit includes 72 bits of payload + 8 bits of CRC.

## Slide 151: 3.4 Layout of the interconnect links (7)
Message classes in the QPI protocol
In the QPI protocol protocol events are grouped into message classes.
There are the following seven message classes defined [70]:
Figure: Message classes defined for the QPI [67]
Messages are subdivided into packets.

## Slide 152: 3.4 Layout of the interconnect links (8)
Main features of the message classes [71]

## Slide 153: 3.4 Layout of the interconnect links (9)
Sending messages over virtual channels to the Link layer [69]
Link layer

## Slide 154: 3.4 Layout of the interconnect links (10)
Credit-based flow control [72]
Avoiding deadlocks while sending packets or flits is credit based.
This means:
During initialization, a sender is given a number of credits for each available
channel to send packets, or Flits to a receiver.
Whenever a packet or Flit is sent to the receiver over a channel, the sender
decrements its related credit counter by one credit.
Credits are returned from the receiver link layer after it has gated the data
sent, freed the related buffer and is ready to receive more information.
Figure: Principle of credit based flow control in Intel's QPI [72]

## Slide 155: 3.4 Layout of the interconnect links (11)
Example of a QPI packet with interleaved “command insert” packets [71]
There are three “command insert” packets, labeled 5, 8, 10 where packet 5
comprises two flits.
Furthermore, special packets 6 and 7 are interleaved between the flits of the
“command insert” packet.

## Slide 156: 3.4 Layout of the interconnect links (12)
Example 2: IBM’s 2-level, local and global inter-processor links in in the
POWER8-based E880 systems -1 [67]
IBM makes use of local and
global links in their 2-level
inter-processor interconnects,
as indicated on the right.
Intra-node local links
(1. level links)
Inter-node global links
(2. level links)

## Slide 157: 3.4 Layout of the interconnect links (13)
Example 2: IBM’s 2-level, local and global inter-processor links in the
POWER8-based E880 systems -1 [52]
IBM didn’t disclose any details of the links used, however a related patent granted
to IBM [] allows certain assumptions:
Both the 1. level (intra-node or local) and the 2. level (inter-node or global) links
are point-to-point interconnects.
Individual links (one of three) include a large number of signals (in the order
of 300) as the cited patent discloses (see next Figure):
ventor
  Charles Francis Marino
  John Thomas Holloway, Jr.
  Praveen S. Reddy
  William John Starke

## Slide 158: 3.4 Layout of the interconnect links (14)
1. level (designated in the Figure as nodal) and 2. level (global) links
revealed in the related patent [52]

## Slide 159: 3.4 Layout of the interconnect links (15)
IBM’s 2-level, local and global inter-processor links in the POWER8-based
E880 systems -2 [67]
According to [] the transfer rate of the 1. level links is 76.8 GB/s.
By taking into account the clock rate of about 4 GHz of the discussed system,
and the large number of bits per link (~300) 16B wide datapaths can be
assumed.
Based on the large number of lines per link it can also be speculated that not
differential signaling but voltage referenced signaling was used to reduce
dissipation similarly as in Intel’s Skylake-SP memory links.

## Slide 160
5. Cluster interconnects

## Slide 161: 5. Cluster interconnects (1)
Intra-processor
interconnects
Inter-node
interconnects
Main functional levels of interconnects
Inter-processor
interconnects
Interconnects the functional
units of a processor
P
Per./
IO
GPU
Disp
M
.
Interconnects processors
within a server
(e.g. DP/MP servers) [2]
Interconnects nodes
(e.g. 2P/4P servers) of a processor cluster [3]
5. Cluster interconnects -1

## Slide 162: 5. Cluster interconnects (2)
Cluster interconnects -2
Consequently, for processor clusters that have a large number
(e.g. many tens, hundreds or
thousands) of nodes direct
meshes between the nodes
are not more practicable.
Figure: Direct connect full mesh of an
8-node multiprocessor (actually IBM’s
Power 595 8-node multiprocessor) [66]
With higher number of nodes (that may include one or a few (e.g. 4) processors), direct meshes between the nodes become more and more complex as n nodes
require for a full mesh n * (n-1)/2 bidirectional links (as seen in the Figure below).

## Slide 163: 5. Cluster interconnects (3)
Remark
Processor clusters are used for HPC or for enterprises purposes (e.g. large
database systems).
In fact, about 40 % of the top 500 computers are processor clusters of many
hundreds or thousands of nodes.

## Slide 164: 5. Cluster interconnects (4)
For the reason discussed before, nodes of a processor cluster are not more
interconnected directly by a partial or full mesh but indirectly via switches,
as e.g. indicated below.
Cluster interconnects -2
Figure: Interconnecting nodes of a cluster that is subdivided into subnets, indirectly,
by switches [73]

## Slide 165: 5. Cluster interconnects (5)
Cluster interconnects -3
Processor clusters is a complex topics of its own, we don’t go into details.
Instead we provide a glimpse of it by showing examples of particular points of it.

## Slide 166
High speed interconnection technologies used in cluster interconnects
Ethernet
Fibre channel (FC) (to connect SANs (Storage Area Networks) to servers)
InfiniBand (IB)
Intel’s OmniPath
5. Cluster interconnects (6)

## Slide 167
Evolution of InfiniBand based high speed interconnect technology to
Intel’s OmniPath
Infiniband (InfiniBand Trade Association. 1999)
TrueScale (Qlogic 2008)
(HPC Enhanced version of InfiniBand)
1/2012 Intel acquires QLogic’s TrueScale business
At the 2014 International Supercomputing Conference Intel announces both
Knights Landing and
the OmniScale interconnect fabric
11/2014 Intel renames OmniScale to OmniPath
5. Cluster interconnects (7)
06/2016 Intel's Knights Landing line with in-package integrated OmniPath host channel adapter
07/2017 Intel's Xeon Skylake-SP line with in-package integrated OmniPath host channel adapter

## Slide 168: 5. Cluster interconnects (8)
Omni-Path host adapter (to be inserted into a PCIe slot) [74]

## Slide 169: 5. Cluster interconnects (9)
48-port Omni-Path switch in an 1U rack [75]

## Slide 170
Implementation alternatives of the Host Fabric Interfaces (HFI)
Implementation
on a separate card
In-package integration
(Implementation as a
Multi-Chip Package (MCM))
On-chip integration
1. Gen. Knights Landing
with OmniPath HCA
Skylake-F
2. Gen. Knights Landing
with OmniPath HCA
Previous systems
with TrueScale
Examples:
Evolution of the implementation of Host Channel Adapters (HCAs) called
Host Fabric Interfaces (HFIs) in OmniPath in Intel’s processors
5. Cluster interconnects (10)
*

## Slide 171: 5. Cluster interconnects (11)
System software needed for a cluster interconnect fabric [76]

## Slide 172
5. References

## Slide 173
[1]: Intel Calls for 3D IC, EE Times, March 5 2015,
https://www.eetimes.com/author.asp?section_id=36&doc_id=1325921&image_number=1
5. References (1)
[3]: Supermicro Motherboards, MNL-1594X6QT8, User Manual,
https://www.supermicro.com/manuals/motherboard/C606_602/MNL-1594.pdf
[4]: Lau J., MCM, SiP, SoC, and Heterogeneous Integration Defined and Explained, 3DInCities,
Aug. 7 2017, https://www.3dincites.com/2017/08/mcm-sip-soc-and-heterogeneous-
integration-defined-and-explained/
[5]: Intel quadcore Xeon 5300 review, Nov. 13 2006, Hardware.Info,
http://www.hardware.info/en-US/articles/amdnY2ppZGWa/Intel_quadcore_Xeon_5300_review
[6]: Wasson S., Intel's Woodcrest processor previewed, The Bensley server platform debuts,
May 23, 2006, The Tech Report, http://techreport.com/articles.x/10021/1
[2]: Esmer I., Ivybridge Server Architecture: A Converged Server, Aug. 2014, Hot Chips 2014,
http://www.hotchips.org/wp-content/uploads/hc_archives/hc26/HC26-12-day2-epub/
HC26.12-8-Big-Iron-Servers-epub/HC26.13.832-IvyBridge-Esmer-Intel-IVB%20Server%
20Hotchips2014.pdf
[7]: Teich P., The Heart Of AMD’s Epyc Comeback Is Infinity Fabric, The Next Platform, July 12 2017,
https://www.nextplatform.com/2017/07/12/heart-amds-epyc-comeback-infinity-fabric/
[8]: Kennedy P., AMD EPYC Infinity Fabric Update and MCM Cost Savings, STH, Aug. 22 2017,
https://www.servethehome.com/amd-epyc-infinity-fabric-update-mcm-cost-savings/
[9]: MCM-GPU: Multi-Chip-Module GPUs for Continued Performance Scalability, Nvidia,
http://research.nvidia.com/publication/2017-06_MCM-GPU%3A-Multi-Chip-Module-GPUs

## Slide 174
[10]: Altavilla D., Intel Arrandale Core i5 and Core i3 Mobile Unveiled, Hot Hardware, Jan. 4 2010,
http://hothardware.com/Reviews/Intel-Arrandale-Core-i5-and-Core-i3-Mobile-Unveiled
5. References (2)
[12]: Scansen D., Intel Launches Next Generation of Microprocessors, Engineering, June 10 2013,
http://www.engineering.com/ElectronicsDesign/ElectronicsDesignArticles/ArticleID/
5838/Intel-Launches-Next-Generation-of-Microprocessors.aspx
[13]: Mujtaba H., Intel Knights Landing Further Detailed – 16 GB High-Bandwidth On-Package
Memory, 384 GB DDR4 System Memory Support and 8 Billion Transistors, WCCF Tech,
March 26 2015, https://wccftech.com/intel-knights-landing-detailed-16-gb-highbandwidth-
ondie-memory-384-gb-ddr4-system-memory-support-8-billion-transistors/
[14]: Maxfield M., Design How-To, 2D vs. 2.5D vs. 3D ICs, EE Times, April 8 2012,
https://www.eetimes.com/document.asp?doc_id=1279540
[15]: Solberg V., 2.5D and 3D Semiconductor Package Technology: Evolution and Innovation,
http://www.circuitinsight.com/pdf/2.5d_3d_semiconductor_package_technology_ipc.pdf
[11]: Stoerchle M., IBM System z10 Technologie, 2008,
https://www.guug.de/lokal/muenchen/2008-11-10/IBM_System_z_guug.pdf
[16]: Conolly C., „Intel Paxville Dual Core Xeon and the ASsus PVL-D Intel 7520,” Oct. 2005,
http://www.gamepc.com/labs/view_content.asp?id=paxville&page=1
[17]: Douglas J., „Intel 8xx series and Paxville Xeon-MP Microprocessors,”
http://www.hotchips.org/archives/hc17/3_Tue/HC17.S8/HC17.S8T1.pdf
[18]: Alcorn P., Hot Chips 2017: Intel Deep Dives Into EMIB, Tom’s Hardware, Aug. 25 2017,
https://www.tomshardware.com/news/intel-emib-interconnect-fpga-chiplet,35316.html

## Slide 175
[19]: Marcoux P., 2.5D, Silicon Interposers, Silicon Bridges, Glass Panels, Organic HDI,
http://www.meptec.org/Resources/1%20-%20ALLVIA%20-%20Marcoux.pdf
5. References (3)
[21]: Pirzada U., Intel and Altera Develop World’s First HBM2, 2.5D Stacked, SiPs With Integrated
Stratix 10 FPGA and SoC Solution, WCCF Tech, Nov. 17 2015,
https://wccftech.com/intel-altera-offering-hbm2-fpga-sip-stratix-10/
[22]: Demerjian C., Intel Kaby-G with “Not AMD” Radeon Vega M graphics fleshed out, Semi
Accurate, Jan. 7 2018, https://semiaccurate.com/2018/01/07/intel-kaby-g-not-amd-
radeon-vega-m-graphics-fleshed/
[23]: Embedded Multi-die Interconnect Bridge, Intel,
https://www.intel.com/content/www/us/en/foundry/emib.html
[24]: von Appen S., Hotti M., Hybrid Memory Cube, Micron Technology Inc., July 2017
[20]: Mahajan R., Sankman R., et al., Embedded Multi-die Interconnect Bridge (EMIB) -- A High
Density, High Bandwidth Packaging Interconnect, IEEE 66th ECTC, 2016
[25]: Kumar A., Trivedi M., Intel Xeon Scalable Processor Architecture Deep Dive, June 12 2017,
https://www.primeline-solutions.de/files/intel-xeon-scalable-architecture-deep-dive_1.pdf
[26]: Heidekrüger A., CPU / GPU Technologies Now and Future, 2010,
http://www.hpcadvisorycouncil.com/events/2011/switzerland_workshop/pdf/Presentations/
Day%202/10_AMD_CPU.pdf
[27]: Anthony S., Intel unveils 72-core x86 Knights Landing CPU for exascale supercomputing,
Extremetech, Nov. 26 2013, http://www.extremetech.com/extreme/171678-intel-unveils-
72-core-x86-knights-landing-cpu-for-exascale-supercomputing

## Slide 176
[28]: Anthony S., ARM says $20 smartphones coming this year, shows off 64-bit Cortex-A53 and
A57 performance, Extreme Tech, May 6 2014,
http://www.extremetech.com/computing/181935-arm-says-20-smartphones-coming-
this-year-shows-off-64-bit-cortex-a53-and-a57-performance
5. References (4)
[29]: Frumusanu A., The Samsung Exynos 7420 Deep Dive - Inside A Modern 14nm SoC,
AnandTech, June 29 2015, http://www.anandtech.com/show/9330/exynos-7420-deep-dive
[30]: Merritt R., ARM stretches out with A5 core, graphics, FPGAs, Oct. 21 2009,
http://www.embedded.com/print/4085371
[31]: Etienne S., Nvidia’s GTX 1050 3GB graphics card will cater to the budget PC gamer,
The Verge, May 23 2018, https://www.theverge.com/circuitbreaker/2018/5/23/17384410/
nvidia-gtx-1050-card-budget-diy-pc-gaming
[32]: Pikalov S., Intel 965 Express Chipsets with Official Support for Core 2 Duo/Extreme,
IXBT Labs, Sept. 14 2006, http://ixbtlabs.com/articles2/mainboard/i965-chipset.html
[33]: Intel X58 Express Chipset Product Brief, Intel, 2008,
https://www.intel.com/Assets/PDF/prodbrief/x58-product-brief.pdf
[34]: Intel Q57 Express Chipset Product Brief, Intel, 2009,
http://www.hard-net.de/info_wissen/chipsatz/intel/Q57.pdf
[35]: Intel Q67 Express Chipset, http://www.intel.com/content/www/us/en/chipsets/mainstream-
chipsets/q67-express-chipset.html

## Slide 177
[36]: Unparalleled Performance and Responsiveness, Product Brief, Intel Z87 Chipset, 2013,
http://www.intel.com/content/dam/www/public/us/en/documents/product-briefs/
z87-chipset-brief.pdf
5. References (5)
[37]: Cutress I., Intel Z87 Motherboard Review with Haswell: Gigabyte, MSI, ASRock and ASUS,
AnandTech, June 27 2013, https://www.anandtech.com/show/6989/intel-z87-
motherboard-review-with-haswell-gigabyte-msi-asrock-and-asus-at-200
[38]: Kampman J., Intel product brief spills the beans on the Z390 chipset, Tech Report,
May 14 2018, https://techreport.com/news/33634/intel-product-brief-spills-the-beans-
on-the-z390-chipset
[39]: Intel Core M Processor Family Datasheet, Sept. 2014,
https://www.intel.in/content/dam/www/public/us/en/documents/datasheets/core-m-
processor-family-datasheet-vol-1.pdf
[40]: Yuffe M., Knoll E., Mehalel M., Shor J., Kurts T., A fully integrated multi-CPU, GPU and
memory controller 32nm processor, ISSCC, Febr. 20-24 2011, pp. 264-266
[41]: Morgan T. P., Intel Puts More Compute Behind Xeon E7 Big Memory, The Platform,
May 5 2015, http://www.theplatform.net/2015/05/05/intel-puts-more-compute-behind-
xeon-e7-big-memory/
[42]: Wasson S., Inside ARM's Cortex-A72 microarchitecture, TechReport, May 1 2015,
http://techreport.com/review/28189/inside-arm-cortex-a72-microarchitecture
[43]: 64 Bit Juno ARM® Development Platform, ARM, 2014,
https://www.arm.com/files/pdf/Juno_ARM_Development_Platform_datasheet.pdf

## Slide 178
[44]: CoreLink CCI-400 Cache Coherent Interconnect, Technical Reference Manual, 2011,
http://infocenter.arm.com/help/topic/com.arm.doc.ddi0470c/DDI0470C_cci400_r0p2_trm.pdf
5. References (6)
[45]: Lacouvee D., Fact or Fiction: Android apps only use one CPU core, May 25 2015,
http://www.androidauthority.com/fact-or-fiction-android-apps-only-use-one-cpu-core-
610352/
[46]: Wikipedia, Advanced Microcontroller Bus Architecture,
https://en.wikipedia.org/wiki/Advanced_Microcontroller_Bus_Architecture
[47]: Stevens A., Introduction to AMBA 4 ACE and big.LITTLE Processing Technology, White Paper,
June 6 2011, https://www.arm.com/files/pdf/CacheCoherencyWhitepaper_6June2011.pdf
[48]: AMBA, Advanced Microcontroller Bus Architecture Specification, Document Number:
ARM IHI 0001D, April 1997
[49]: Andrews J. R., Co-Verification of Hardware and Software for ARM SoC Design,
Elsevier Inc. 2005
[50]: Intel PXA270 Processor Data Sheet, 2006, https://docs.toradex.com/100210-colibri-arm-
som-pxa270-electrical-mechanical-specification.pdf
[51]: Stuecheli J., POWER8, Hot Chips, 2013, http://www.hotchips.org/wp-content/uploads/
hc_archives/hc25/HC25.20-Processors1-epub/HC25.26.210-POWER-Studecheli-IBM.pdf
[52]: US7917730B2 patent, inventors Marino C.F. et al., Processor chip with multiple computing
elements and external i/o interfaces connected to perpendicular interconnection trunks
communicating coherency signals via intersection bus controller, Assignee IBM, 2011,
https://patents.google.com/patent/US7917730

## Slide 179
[53]: Multi-Layer AHB, AHB-Lite,
http://www.13thmonkey.org/documentation/ARM/multilayerAHB.pdf
5. References (7)
[54]: Multi-layer AHB Overview, DVI 0045A, ARM Limited, 2001,
http://pdf.datasheetarchive.com/indexerfiles/Datasheets-SL1/DSASL001562.pdf
[55]: ARM CoreLink NIC-400 Network Interconnect, Technical Reference Manual, Rev. r0p3,
2012-2014, https://static.docs.arm.com/ddi0475/e/DDI0475E_corelink_nic400_network_
interconnect_r0p3_trm.pdf
[56]: ARM Cortex-A7, http://www.arm.com/products/processors/cortex-a/cortex-a7.php
[57]: Multi-core and System Coherence Design Challenges,
http://www.ece.cmu.edu/~ece742/f12/lib/exe/fetch.php?media=arm_multicore_and_
system_coherence_-_cmu.pdf
[58]: Intel Xeon Phi Coprocessor Datasheet, Nov. 2012, http://www.intel.com/content/dam/
www/public/us/en/documents/product-briefs/xeon-phi-datasheet.pdf
[59]: Cheng M., Freescale QorlQ Product Family Roadmap, APF-NET-T0795, April 2013,
https://www.nxp.com/files-static/training/doc/dwf/DWF13_APF_NET_T0795.pdf
[60]: CoreLink CCN-504 Cache Coherent Network,
http://www.arm.com/products/system-ip/interconnect/corelink-ccn-504-cache-coherent-
network.php
[61]: Parris N., Boost SoC performance from edge to cloud ARM CoreLink System IP, ARM,
Nov. 2016, http://www.armtechforum.com.cn/attached/article/2016ATS_C1_Neil_Parris
20161206151154.pdf

## Slide 180
[62]: Chiappetta M., Intel Xeon Scalable Debuts: Dual Xeon Platinum 8176 With 112 Threads
Tested, Hot Hardware, July 11 2017,
https://hothardware.com/reviews/intel-xeon-scalable-processor-family-review
5. References (8)
[63]: De Gelas J., New ARM IP Launched: CMN-600 Interconnect for 128 Cores and DMC-620, an
8Ch DDR4 IMC, AnandTech, Sept. 27 2016, https://www.anandtech.com/show/10711/
arm-cmn-600-dmc-620-128-cores-8-channel-ddr4
[64]: System Guidance for Infrastructure, ARM Developer,
https://developer.arm.com/products/system-design/system-guidance/system-guidance-
for-infrastructure
[65]: De Gelas J., Cutress I., Sizing Up Servers: Intel's Skylake-SP Xeon versus AMD's EPYC
7000 - The Server CPU Battle of the Decade?, AnandTech, July 11 2017,
https://www.anandtech.com/show/11544/intel-skylake-ep-vs-amd-epyc-7000-cpu-battle-
of-the-decade/23
[66]: IBM Power 595 Technical Overview and Introduction, Red Paper, Aug. 2008,
http://www.redbooks.ibm.com/redpapers/pdfs/redp4440.pdf
[67]: IBM Power Systems E870 and E880 Technical Overview and Introduction, Red Paper,
Dec. 2014, http://www.redbooks.ibm.com/redpapers/pdfs/redp5137.pdf
[68]: Nikhil R. S., A programming/specification and verification problem based on the Intel QPI
protocol (“QuickPath Interconnect”), IFIP Working Group 2.8, 27th meeting, Shirahama,
Japan April 2010,
http://www.cs.ox.ac.uk/ralf.hinze/WG2.8/27/slides/rishiyur1.pdf

## Slide 181
[69]: Ng P. K., “High End Desktop Platform Design Overview for the Next Generation Intel
Microarchitecture (Nehalem) Processor,” IDF Taipei, TDPS001, 2008,
http://intel.wingateweb.com/taiwan08/published/sessions/TDPS001/FA08%20IDF-
Taipei_TDPS001_100.pdf
5. References (9)
[70]: Safranek R., Intel QuickPath Interconnect Overview, Hot Chips 21, 2009,
https://www.hotchips.org/wp-content/uploads/hc_archives/hc21/1_sun/HC21.23.1.
SystemInterconnectTutorial-Epub/HC21.23.120.Safranek-Intel-QPI.pdf
[71]: Safranek R., Moravan M., QuickPath Interconnect: Rules of the Revolution, Dr. Dobbs Go
parallel, Nov. 4 2009,
http://www.drdobbs.com/go-parallel/article/print?articleId=221600290
[72]: An Introduction to the Intel QuickPath Interconnect, Document Number: 320412-001US,
Jan. 2009, http://www.intel.com/content/www/us/en/io/quickpath-technology/quick-
path-interconnect-introduction-paper.html
[73]: Fiber Transceiver Solution,
http://www.fiber-optic-transceiver-module.com/things-you-should-know-about-infiniband.html
[74]: Wasson S., Intel reveals details of its Omni-Path Architecture interconnect, TechReport,
Aug. 26 2015, http://techreport.com/news/28908/intel-reveals-details-of-its-omni-path-
architecture-interconnect
[75]: Kennedy P., Supermicro releases new high-density storage and Omni-Path products,
ServeTheHome, Nov. 16 2015, http://www.servethehome.com/supermicro-releases-new-
high-density-storage-and-omni-path-products/
[76]: Birrittella M. S., Intel Omni-Path Architecture Technology Overview, August 2015,
http://www.hoti.org/hoti23/slides/rimmer.pdf

## Slide 182
[77]: Intel Core i5-8600 3.1 GHz Review, TechPower, Apr. 25, 2018,
https://www.techpowerup.com/reviews/Intel/Core_i5_8600/3.html
5. References (10)
[78]: Alcorn P., Intel Plays Defense: Inside Its EPYC Slide Deck, Tom’s Hardware, July 17, 2017,
https://www.tomshardware.com/reviews/intel-amd-die-fabric-slides,5125-3.html
[79]: Microsystems Integration, Aug. 28-Sept. 2 2014,
http://www.colorado.edu/engineering/MCEN/MCEN5166/Lectures/MI_2_iPhone2_
1st2ndPKG_2014_Aug28.pdf
[80]: Dreiza M., Kim J.S., Smith L., Campos D., Saugier E. Jarvinen P., Joint Project for Mechanical
Qualification of Next Generation High Density Package-on-Package (PoP) with Through
Mold Via Technology, EMPC2009 – 17th European Microelectronics & Packaging Conference,
June 16 2009, Rimini, Italy
[81]: Apple A4 Teardown. iFixit,
https://www.ifixit.com/Teardown/Apple+A4+Teardown/2204