## Slide 1
Dezső Sima
November 2019
(Ver. 1.1)
 Sima Dezső, 2019
High-End
2S Server Processors and Platforms

## Slide 2: High-end 2S server processors and platforms (1)
Remarks
a) The material presented in these slides is restricted to multicore server processors,
previous single core server processors were omitted.
Due to this presumtion, subsequently, we do not repeatedly state the above
restriction throughout this Chapter.
b) Further on, to reduce the volume of this Chapter, we discuss only Intel’s and
AMD’s processor lines.
Intel's server families
Xeon servers
Itanium servers
x86 ISA
(1998 - recently)
IA-64 ISA
(2001 - 2017)
As far as Intel’s server processor lines are concerned, we discuss mainly
Intel’s high-end 2S (two socket) x86 server processors (called Xeons) and
platforms.
Previous single core designs, Intel’s „efficient performance” and „entry level”
as well as IA64 (Itanium) based processors and platforms are not covered.
On the other hand, from AMD’s designs we discuss only the EPYC line of multicore server processors (introduced in 2017).
Their ill-fated Bulldozer server lines (2011-2016) are omitted.

## Slide 3
High-end 2S server processors and platforms
1. Introduction to server processors and platforms
2. Overview of Intel’s high-end multicore 2S server proc.s
5. AMD’s Zen-based 2S server processors
3. The risk of arising memory bandwidth bottleneck
in multicore server processors
4. Intel’s high-end multicore 2S server processors
7. References
6. Platform issues of 2S server processors
Section 5. will not be discussed.
Notes: 3

## Slide 4
Introduction to server processors and platforms
1.1 The worldwide server market
1.2 The platform concept
1.3 Classification of server platforms
1.4 Naming schemes of Intel’s and AMS’s server processors
Notes: 4

## Slide 5: Introduction to server processors and platforms (1)
Introduction to server processors and platforms
Figure: Recent datacenter [1]

## Slide 6: Introduction to server processors and platforms (2)
Example for the hierarchical layout of data centers [47]

## Slide 7
1.1 The worldwide server market
Notes: 7

## Slide 8: 1.1 The worldwide server market (1)
Recent market share of 1S and 2S servers [2]
1.1 The worldwide server market (1)

## Slide 9: 1.1 The worldwide server market (2)
The worldwide 4S (4-socket) server market [3]
*
MSS: Market Segment Share

## Slide 10: 1.1 The worldwide server market (3)
Intel's vs AMD's x86 server market share (Based on data by IDC [4]
Core 2 Quad DP
Penryn DP
Penryn MP
Nehalem-EX DP/MP
Core 2 DP
K10 Barcelona MP
K10 Shanghai MP
K10 Magny Course MP
K10 Istambul MP

## Slide 11: 1.1 The worldwide server market (4)
Intel's vs AMD's x86 server market share (Based on data from [193]

## Slide 12: 1.1 The worldwide server market (5)
Remark
In 06/2017 AMD launched their EPYC server processor line supporting at its
introduction 2-socket configurations.
EPYC server processors are based on the Zen microarchitecture.
Time will show how far AMD will be able to gain market share against Intel's
latest, Cascade Lake-SP/AP based servers.
*

## Slide 13: 1.1 The worldwide server market (6)
Vendor | 1Q16 Revenue | 1Q16 Market Share | 1Q16/1Q15 Revenue Growth
1. HP | $3,306.8 | 26.7% | 3.5%
2. Dell | $2,267.8 | 18.3% | -1.8%
3. IBM | $1,139.5 | 9.2% | -32.9%
4. Lenovo * | $871.2 | 7.0% | -8.6%
5. Cisco * | $850.2 | 6.9% | -4.5%
ODM Direct | $863.8 | 7.0% | -11.0%
Others | $3,082.4 | 24.9% | 9.0%
Total | $12,382 | 100% | -3.6%
Top 5 worldwide server systems vendors, their revenues, market shares
and growth in Q1 2016 (Revenues are in Millions USD) [5]
HPE: HP Enterprise
Source: IDC's Worldwide Quarterly Server Tracker, June 2016

## Slide 14
1.2 The platform concept
Notes: 14

## Slide 15: 1.2 The platform concept (1)
1.2 The platform concept
The notion platform is widely used in different segments of the IT industry e.g.
by IC manufacturers, system providers or even by software suppliers with
different interpretations.
Here we are focusing on the platform concept as used by system providers, like
Intel or AMD.
The platform concept of system providers
Remark
The designation platform is often understood as the entire system architecture.
*
A platform is a skeleton of a system architecture those basic components are:
interchangeable processor models i.e. processors with the same interfaces
and socket (like the Ivy Bridge-EX, Haswell-EX and Broadwell-EX processors),
a matching chipset and
the platform topology.

## Slide 16: 1.2 The platform concept (2)
Platform | Core | Techn. | Introced | 2S server line | Chipset | Processor socket
 | Pentium 4 Presc. DP | 90 nm | 6/2004 | 90 nm Nocona | E7520+ ICH5R/6300ESB | mPGA 604
 | Pentium 4 Presc. 2M DP | 90 nm | 10/2005 | Xeon DP 2.8 (Paxville DP) |  | 
Bensley | Pentium 4 Presc. 2M DP | 65 nm | 5/2006 | Xeon 5000 (Dempsey) | 5000+ 631xESB/632xESB | LGA 771
 | Core2 | 65 nm | 6/2006 | Xeon 5100 (Woodcrest) |  | 
 | Core2 | 65 nm | 11/2006 | Xeon 5300 (Clowertown) |  | 
 | Penryn | 45 nm | 11/2007 | Xeon 5400 (Harpertown) |  | 
Boxboro-EX | Nehalem | 45 nm | 3/2010 | Xeon X6500 Nehalem-EX) | 7500+ ICH10 | LGA 1567
 | Westmere | 32 nm | 4/2011 | Xeon E7-28xx (Westmere-EX) |  | 
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-28xx v2 (Ivy Bridge-EX) | C600 (Pattsburg) | LGA 2011-1
Grantley | Haswell | 22 nm | 9/2014 | E5-2600xx v3 (Haswell-EP) | C612 (Wellsburg) | LGA 2011-3
 | Broadwell | 14 nm | 4/2016 | E5-26xx v4 (Broadwell-EP) |  | 
Purley | Skylake | 14 nm | 7/2017 | Silver 41xx (Skylake-SP) | C621/622 (Lewisburg) | LGA 3647
 | Cascade Lake | 14 nm | 4/2019 | Silver 42xx Cascade Lake-SP |  | 
na. | Cascade Lake | 14 nm | 4/2019 | Platinum 92xx Cascade Lake-AP |  | BGA 5903
Example: Intel’s x86-based high-end 2S server platforms

## Slide 17: 1.2 The platform concept (3)
Compatibility of platform components (2)
Since platform components are connected via specified interfaces, platform
components, such as processors or memories are compatible to a given platform
as long as they have the same interfaces (including interface parameters, such as
transfer rates etc.).
*

## Slide 18: 1.2 The platform concept (4)
Nehalem-EX 8C
Westmere-EX 10C
7500 IOH
QPI
QPI
QPI
QPI
QPI
QPI
QPI
QPI
SMB
SMB
Nehalem-EX: up to DDR3-1067
Westmere-EX: up to DDR3-1333
SMB
SMB
SMB
SMB
SMB
SMB
ICH10
ESI
SMI: Scalable Memory Interface
(Serial link between the processor
and the SMB)
SMB: Scalable Memory Buffer
(Performs conversion between the
serial SMI and the parallel
DDR3 DIMM interfaces)
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI
channels
2x4 SMI
channels
Example: Interface requirements for compatible platform components
ME
ME: Management Engine
Xeon 7500
(Nehalem-EX)
(Becton) 8C
Xeon E7-8800
(Westmere-EX) 10C
Nehalem-EX 8C
Westmere-EX 10C
Nehalem-EX 8C
Westmere-EX 10C
Nehalem-EX 8C
Westmere-EX 10C
/
Figure: The Boxboro-EX MP server platform supporting Nehalem-EX/Westmer-EX
server processor
2 DIMMs/memory channel
4 x QPI up to 6.4 GT/s
36
PCIe
2.0

## Slide 19
1.3 Classification of server platforms
Notes: 19

## Slide 20: 1.3 Classification of server platforms (1)
1.3 Classification of server platforms
Classification according to
the number of chips
constituting the chipset
Classification according to
the number of processors
constituting the platform
Classification according to
their topology
Classification of server platforms
*

## Slide 21: 1.3 Classification of server platforms (2)
a) Classification of server platforms according to their topology
SMPs
(Symmetrical MultiProcessor)
Classification of server platforms according to their topology
NUMAs
Multiprocessors (Multi socket system)
with Non-Uniform Memory Access
Multiprocessors (Multi socket system)
with Uniform Memory Access (UMA)
Typical examples
ICH
FSB
E.g. DDR2-533
ESI
E.g. DDR3-1333
Processor
IOH1
QPI
QPI
ICH
ESI
QPI
E.g. DDR3-1333
Processor
Processors access main memory via the chipset.
(Memory controller on the MCH die).
Then all processors access main memory
by the same mechanism, (e.g. by individual
FSBs and an MCH).
1ICH: I/O hub
(Enterprise System Interf.)
Each processor access main memory directly.
(Memory controllers on the processor dies).
Then each processor is allocated a part of the memory
(with the related memory space), called the local memory,
whereas the rest is considered as the remote memory.
Processor
Processor
MCH
*

## Slide 22: 1.3 Classification of server platforms (3)
SMPs
(Symmetrical MultiProcessor)
NUMAs
All processors share the same memory space.
All processors share the same memory space.
Classification of server platforms according to their topology
Main features of SMP-type and NUMA-type server platforms
Consequently, all processors access memory
basically with the same latency.
The local part of the main memory can be accessed
by each processor immediately, e.g. via their
private on-die memory controller,
whereas remote parts of the main memory will be
accessed via the processor owing the requested
memory part.
Processors access their local memory space
with a significantly shorter latency than their
remote memory space, consequently, processors
access main memory with different latencies.
*

## Slide 23: 1.3 Classification of server platforms (4)
Example of measured read latencies of uncached data [6]
Read latencies depend on whether referenced data is kept in the own or remote
main memory space.
a) Read latency of uncached data if referenced data is in the own memory space
Read latency:
65.1 ns (190 cycles)
IMC: Integrated Memory Controller

## Slide 24: 1.3 Classification of server platforms (5)
b) Read latency of uncached data when referenced data is kept in the remote
memory space [6]
Read latency:
106 ns (~310 cycles)
Read latency is now increased now by the inter-processor access penalty of 41 ns.

## Slide 25: 1.3 Classification of server platforms (6)
Platform | Core | Techn. | Date of Intro. | High-end multicore 2S server lines | Chipset | Processor socket
 | Pentium 4 Presc. DP | 90 nm | 6/2004 | 90 nm Nocona | E7520+ ICH5R/6300ESB | mPGA 604
 | Pentium 4 Presc. 2M DP | 90 nm | 10/2005 | Xeon DP 2.8 (Paxville DP) |  | 
Bensley | Pentium 4 Presc. 2M DP | 65 nm | 5/2006 | Xeon 50xx (Dempsey) | 5000+ 631xESB/632xESB | LGA 771
 | Core2 | 65 nm | 6/2006 | Xeon 51xx (Woodcrest) |  | 
 | Core2 | 65 nm | 11/2006 | Xeon 53xx (Clowertown) |  | 
 | Penryn | 45 nm | 11/2007 | Xeon 54xx (Harpertown) |  | 
Example 1: Intel’s high-end 2S multicore SMP server platforms

## Slide 26: 1.3 Classification of server platforms (7)
Platform | Core | Techn. | Date of Intro. | High-end multicore 2S server lines | Chipset | Processor socket
Tylersburg | Nehalem | 45 nm | 3/2009 | Xeon 55xx (Nehalem –EP) Gainestown) | 55xx+ ICH9/ICH10 | LGA 1366
Boxboro-EX | Nehalem | 45 nm | 3/2010 | Xeon 65xx Nehalem-EX) | 75xx+ ICH10 | LGA 1567
 | Westmere | 32 nm | 4/2011 | Xeon E7-28xx (Westmere-EX) |  | 
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-28xx v2 (Ivy Bridge-EX) | C602 (Pattsburg) | LGA 2011-1
Grantley | Haswell | 22 nm | 9/2014 | E5-26xx v3 (Haswell-EP) | C612 (Wellsburg) | LGA 2011-3
 | Broadwell | 14 nm | 4/2016 | E5-26xx v4 (Broadwell-EP) |  | 
Purley | Skylake | 14 nm | 7/2017 | Silver 41xx (Skylake-SP) | C621/C622 (Lewisburg) | LGA 3647
 | Cascade Lake | 14 | 4/2019 | Silver 42xx Cascade Lake-SP |  | 
?? | Cascade Lake | 14 | 4/2019 | Platinum 92xx Cascade Lake-AP |  | BGA 5903
Example 2: Intel’s high-end 2S multicore NUMA server platforms

## Slide 27: 1.3 Classification of server platforms (8)
b) Classification of server platforms according to the number of processors
constituting the platform
2S (DP)
server platforms
Classification of server platforms
according to the number of processors constituting the platform
Platforms for more than 4 or 8 sockets
2- processor server platforms
(2-socket server platforms)
4S/8S (MP)
server platforms
4/8-processor server platforms
(4/8-socket server platforms)
Server platforms for
more than the Intel
supported number of
sockets
(4 or 8 sockets)
They need third party
node controllers
Uniprocessor server platforms
(UP-server platforms)
1-processor server platforms
(1-socket server platforms)
Multiprocessor server platforms
Server platforms supporting more than one processor
(Multi-socket server platforms)
Truland-MP platform
Caneland MP platform and
4S platforms
8S platforms
E5-4600, v2, v3, v4
E7-4800, v2, v3, v4
subsequent platforms with
processors
Platforms with
E7-8800, v2, v3, v4
processors
E5-2600, v2, v3, v4
E7-2800, v2,
platforms with
processors
Early DP platforms and
*

## Slide 28: 1.3 Classification of server platforms (9)
Platforms with
two-chip chipsets
Classification of platforms according to the number of chips constituting the chipset
Platforms with
single-chip chipsets
c) Classification of platforms according the number of chips constituting
the chipset
Truland platform (2005/2006)
Caneland platform (2007/2008)
Boxboro-EX platform (2010/2011)
Brickland platform (2014/2015)
Purley platform (2017)
Platforms without
a chipset
(AMD's 2S platform
With EPYC-7000 series processors)
*

## Slide 29: 1.3 Classification of server platforms (10)
Nehalem-EX 8C
Westmere-EX 10C
7500 IOH
QPI
QPI
QPI
QPI
QPI
QPI
QPI
QPI
SMB
SMB
Nehalem-EX: up to DDR3-1067
Westmere-EX: up to DDR3-1333
SMB
SMB
SMB
SMB
SMB
SMB
ICH10
ESI
SMI: Scalable Memory Interface
(Serial link between the processor
and the SMB)
SMB: Scalable Memory Buffer
(Performs conversion between the
serial SMI and the parallel
DDR3 DIMM interfaces)
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI
channels
2x4 SMI
channels
Example 1: A platform with a 2-chip chipset: The Boxboro-EX 4S/8S server
platform supporting Nehalem-EX/Westmere-EX processors
ME
ME: Management Engine
Xeon 7500
(Nehalem-EX)
(Becton) 8C
Xeon E7-4800
(Westmere-EX) 10C
Nehalem-EX 8C
Westmere-EX 10C
Nehalem-EX 8C
Westmere-EX 10C
Nehalem-EX 8C
Westmere-EX 10C
/
Nehalem-EX aimed Boxboro-EX MP server platform (for up to 10 C)
2 DIMMs/memory channel
4 x QPI up to 6.4 GT/s
36
PCIe
2.0

## Slide 30: 1.3 Classification of server platforms (11)
Example 2: A a platform with a single-chip chipset: The Brickland-EX 4S/8S server platform for Ivy Bridge-EX/Haswell-EX/Broadwell-EX processors
ME: Management Engine
QPI 1.1: Up to 9.6 GT/s
QPI
1.1
QPI
1.1
QPI 1.1
QPI 1.1
QPI 1.1
QPI 1.1
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI2
channels
2x4 SMI2
channels
Xeon E7-8800 v2/v3/v4
(Ivy Bridge-EX / Haswell-EX /Broadwell-EX)
Haswell-EX 18C
Haswell--EX 18C
Haswell-EX 18C
Haswell-EX 18C
SMI2: Scalable Memory Interface 2
(Parallel 64-bit VMSE data link between
the processor and the SMB)
SMB: Scalable Memory Buffer
(C112/C114: Jordan Creek 2)
(Performs conversion between the
parallel SMI2 and the parallel
DDR3/DDR4 DIMM interfaces)
C112: 2 DIMMs/channel
C114: 3 DIMMs/channel
Up to DDR3-1600
in both performance and lockstep modes and
up to DDR4-1866 in lockstep mode
PCIe 3.0
32
PCIe 3.0
32
C602J PCH
(Patsburg J)
DMI2
4xPCIe2
ME
PCIe 3.0
32
PCIe 3.0
32

## Slide 31: 1.3 Classification of server platforms (12)
64
PCIe 3.0
EPYC 32C
64
PCIe 3.0
EPYC 32C
8 channels
up to DDR4-2666
8 channels
up to DDR4-2666
Example 3: A platform without a chipset: AMD’s 2S server platform
supporting EPYC 7001 processors
4x16 bit
differential
links
AMD EPYC 7001

## Slide 32
1.4 Naming schemes of server processors
Notes: 32

## Slide 33
1.4.1 Naming schemes of Intel’s server processors
Notes: 33

## Slide 34: 1.4.1 Naming schemes of Intel’s server processors (1)
1.6 Naming schemes of Intel’s server processors
Until 2005 Intel named their servers by identifying clock frequency and server
configuration, like Xeon 2.8 GHz DP or Xeon 2.0 GHz MP, since Intel’s IC technology
was superior to their competitors and provided higher clock frequencies.
a) Naming scheme until 2005
Remark
At that time AMD manufactured their processors in their own foundry, with a
less advanced IC technology, so their processors had lower clock frequencies vs.
Intel’s processors.
To hide this deficiency, AMD introduced a new naming scheme for their
processors beginning with their Athlon XP desktop line in 2003.
The new naming scheme consisted of a four digit number and the +character.,
e.g. Athlon 1600+.
AMD interpreted it as the relative performance level related to a given AMD
DT model (Athlon 1.4 GHz).
The relative performance was calculated as the average value of a wide range
of benchmarks.
The actual clock frequencies however, were lower figures, e.g. the
Athlon XP 1600+ had a clock frequency of 1.4 GHz.

## Slide 35: 1.4.1 Naming schemes of Intel’s server processors (2)
.
In the first years of the 2000's clock frequencies became stagnating, as indicated
below [7].
b) Intel’s naming scheme for servers used between 2005 and 2011
Figure: Historical growth of clock rates [7]

## Slide 36: 1.4.1 Naming schemes of Intel’s server processors (3)
9000 series
Intel’s naming scheme introduced for their server processors in 2005
3000 series
5000 series
UP server
lines
Itanium lines
of processors
7000 series
MP server (4S)
lines
DP server (2S)
lines
E.g. Intel named their subsequent MP (4S) server processor lines as follows:
Line | Processor | Based on | Intro
7000 | Paxville MP | Pentium 4 Prescott MP | 2005
7100 | Tulsa | Pentium 4 Prescott MP | 2006
7200 | Tigerton DC | Core 2 | 2007
7300 | Tigerton QC | Core 2 | 2007
7400 | Dunnington | Penryn | 2008
7500 | Beckton | Nehalem | 2010
As an aftermath Intel had to leave its previous naming scheme and introduced
an AMD like naming scheme in 2005, as follows:
b) Intel’s naming scheme for servers used between 2005 and 2011 -2
The drawback of this naming scheme is that it does not reveal any significant
features of the related server families.

## Slide 37: 1.4.1 Naming schemes of Intel’s server processors (4)
Product line: E3, E5 or E7 (E: Enterprise).
Wayness: How many processors are natively supported in a system
Socket type: Signifies processor class (price/performance)
c) Intel's renewed naming scheme for servers (since the Westmere line) -1
In 4/2011 Intel renewed its entire naming scheme to reflect more details in the
designations, as indicated below for server processors.
Figure: Intel’s new Xeon naming scheme [127]
*
Interpretations

## Slide 38: 1.4.1 Naming schemes of Intel’s server processors (5)
EN servers
(Entry level)
Designation of the server classes
EP servers
(Efficient Performance)
E5-24xx
E5-26xx
E5-46xx
EX servers
(Expandable high-end)
E7-28xx
E7-48xx
E7-88xx
Introduction of server classes within a product line (E7/E5/E3)
*

## Slide 39: 1.4.1 Naming schemes of Intel’s server processors (6)
Example 1: E5/E7 processor features of Intel's Ivy Bridge based server
processors [8]
Main differences in the implemented E5-EN, E5-EP and E7-EX Ivy Bridge based server
processors:
 | E5-EN lines | E5- EP lines | E7-EX lines
Type of memory attachment to the on-die MC(s) | Directly attached DDR3 memory channels to a single or dual MCs |  | Memory controlllers are connected to the DIMMs via 4 low line count proprietary 64-bit parallel channels (SMI2 channels) and on-board memory buffers, while 2 DDR3/4 channels are connected to each memory buffer
No. of DDR3 memory channels | 3 DDR3 channels | 4 DDR3 channels | 8 DDR3 channels
No. of QPI links | 1 QPI link | 2 QPI links | 3 QPI links
No. of PCIe lanes | 3x8 lanes | 5x8 lanes | 4x8 lanes
Socket | LGA 1356 | LGA 2011 | LGA 2011-1
PCH | 2S options: C600 (Patsburg) 4S options: C610 (Wellsburg) |  | C602 J (Patsburg J)
*

## Slide 40: 1.4.1 Naming schemes of Intel’s server processors (7)
Example 2: E5/E7 platform options of Ivy Bridge based server processors [8]
Brickland platform (High-end EX platform)
E
Romley platform (Mainstream)
EN: Entry level
EP: Efficient Performance level options

## Slide 41: 1.4.1 Naming schemes of Intel’s server processors (8)
Westmere/Sandy Bridge (without any version number)
v2: Ivy Bridge
v3: Haswell
v4: Broadwell etc.
c) Intel's renewed naming scheme for servers (since the Westmere line) -1
In 4/2011 Intel renewed its entire naming scheme to reflect more details in the
designations, as indicated below for server processors.
Processor SKU: Last two digits of the model number (SKU: Storage Keeping Unit)
Figure: Intel’s new Xeon naming scheme [127]
Version: The same version numbers indicate a common microarchitecture
Interpretations
*

## Slide 42: 1.4.1 Naming schemes of Intel’s server processors (9)
Remarks
The designation of the server generations v2, v3 etc. does not coincides with the
designation of the microarchitecture generations, as shown below:
Microarchitecture | Architecture generation | Server generation
Westmere |  | (without designation), only E7
Sandy Bridge | Gen. 2 | (without designation), only E3/E5
Ivy Bridge | Gen. 3 | v2
Haswell | Gen. 4 | v3
Broadwell | Gen. 5 | v4
2) The Itanium line has not been renamed, it remained the 9000-line, with model
numbers of 9300, 9500, up to 9700.

## Slide 43: 1.4.1 Naming schemes of Intel’s server processors (10)
Haswell
(LGA1150)
Mobiles and desktops
Haswell-E
(LGA2011)
High end desktops
(HEDs)
The Haswell family
Haswell-EP
(LGA2011)
Efficient performance servers, workstations
Haswell-EX
(LG2011)
High-end servers
Servers
Microservers
E3-1275L/1265L v3, 4C+G, HT, 6/2013 and 5/2014
E3-1240L/1230L/1220L v3, 2C/4C, HT, 6/2013 and 5/2014
UP Servers
E3-12x5/12x6 v3, 4C+G, HT, 6/2013 and 5/2014
E3-12x0/12x1 v3, 4C, HT, 6/2013 and 5/2014
E5-16xx v3, 4/6/8C, 9/2014
Workstations
2S-Servers
4S/8S-Servers
E5-26xx v3, 4/6/8/10/12/14/16/18C, 9/2014
E5-46xx v3, 6/10/12/14/16/18C, 6/2015
E7-48xx v3, 8/10/12/14C, 5/2015
E7-88xx v3, 4/10/16/18C, 5/2015
Example 3: The full range of Intel’s server product lines in the Haswell family
Haswell-EN
(LGA1150)
Microservers/
UP servers
Up to 18 cores
E7 designation
Up to 18 cores
E5 designation
Up to 8 cores
i7 designation
Up to 4 cores
i3/i5/i7 designations
Up to 4 cores
E3 designation
E5-24xx v3, 4/6/8/10C, 1/2015

## Slide 44: 1.4.1 Naming schemes of Intel’s server processors (11)
High-end server lines | Models | Scalability | Core count up to | Socket | Intro
Westmere-EX | E7-2800 E7-4800 E7-8800 | 2-socket 4-socket 8-socket | 10C | LGA 1567 | 2011
Ivy Bridge-EX | E7-28xx v2 E7-48xx v2 E7-88xx v2 | 2-socket 4-socket 8-socket | 15C | LGA 2011-1 | 2014
Haswell-EX | E7-48xx v3 E7-88xx v3 | 4-socket 8-socket | 14C 18C | LGA 2011-1 | 2015
Broadwell-EX | E7-48xx v4 E7-88xx v4 | 4-socket 8-socket | 16C 22C | LGA 2011-1 | 2016
Example 4: Intel high-end (EX) server lines

## Slide 45: 1.4.1 Naming schemes of Intel’s server processors (12)
Drawback of the implementation of Intel's - Westmere to Broadwell based - 2S/4S/8S servers
There is a large number of different implementation alternatives of Intel's Westmere
to Broadwell based 2S to 8S server processors, as the next Figure indicates.

## Slide 46: 1.4.1 Naming schemes of Intel’s server processors (13)
Example: E5/E7 platform options of Ivy Bridge based server processors [8]
Brickland platform (High-end EX platform)
E
Romley platform (Mainstream)
EN: Entry level
EP: Efficient Performance level options

## Slide 47: 1.4.1 Naming schemes of Intel’s server processors (14)
d) Intel’s latest naming scheme for servers introduced with the Skylake-SP
line in 2017
It aims at
unifying the processor implementations of the 2S, 4S, 8S configurations,
introducing four performance grades instead of two (E7/E5)
as indicated in the following figures.
*

## Slide 48: 1.4.1 Naming schemes of Intel’s server processors (15)
Unifying the processor implementation of 2S to 8S configurations in Intel’s
Skylake-SP processors [9]
LBG: Lewisburg (PCH)
OP: OmniPath

## Slide 49: 1.4.1 Naming schemes of Intel’s server processors (16)
Introducing four performance grades instead of two (E7/E5) [9]
(4S)
(-SP)
(4S/8S)
Haswell
Broadwell

## Slide 50: 1.4.1 Naming schemes of Intel’s server processors (17)
Corresponding new model namings starting with the Skylake-SP processor
line [10]
(OmniPath)
*
Xeon Platinum supports up to eight sockets,
Xeon Gold supports up to four sockets and
Xeon Silver and Bronze support up to two sockets.
Note

## Slide 51
1.4.2 Naming scheme of AMD’s server processors
Notes: 51

## Slide 52: 1.4.2 Naming scheme of AMD’s server processors (1)
Naming scheme of AMD’s server processors [11]
*

## Slide 53
2. Overview of Intel’s major high-end server processor lines
Notes: 53

## Slide 54
2.1 Key features of Intel’s major high-end server processor lines
Notes: 54

## Slide 55: 2.1 Key features of Intel’s major high-end server processor lines (1)
Subsequently, we summarize key feature of Intel’s 2S and 4S server processor lines and platforms.
2.1 Key features of Intel’s major high-end server processor lines
Intel's first multicore server processors were based on the 3. core of the Pentium 4
processor family (called Prescott), and were introduced about 2005.

## Slide 56: 2.1 Key features of Intel’s major high-end server processor lines (2)
Platform | Core | Techn. | Intro. | High performance Core 2-based multicore 2S server processors | Core count up to | Trans. count [106/109] | Die size [mm2]
 | Pentium 4 Prescott DP | 90 nm | 6/2004 | Xeon DP 90 nm (Nocona) | 1C | 125 | 112
 | Pentium 4 Prescott 2M DP | 90 nm | 10/2005 | Xeon DP 2008 (Paxville DP) | 2x1C | 2x169 | 2x135
Bensley | Pentium 4 Prescott 2M DP | 65 nm | 5/2006 | Xeon 5000 (Dempsey) | 2x1C | 2x188 | 2x81
 | Core2 | 65 nm | 6/2006 | Xeon 5100 (Woodcrest) | 2C | 291 | 143
 | Core2 | 65 nm | 11/2006 | Xeon 5300 (Clovertown) | 2x2C | 2x291 | 2x143
 | Penryn | 45 nm | 11/2007 | Xeon 5400 (Harpertown) | 2x2C | 2x410 | 2x107
Boxboro-EX | Nehalem | 45 nm | 3/2010 | Xeon X6500 (Beckton/Nehalem-EX) | 8C | 2.3 | 513
 | Westmere | 32 nm | 4/2011 | Xeon E7-28xx (Westmere-EX) | 10C | 2.6 | 512
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-28xx v2 (Ivy Bridge-EX) | 15C | 4.31 | 541
 | Haswell | 22 nm | 9/2014 | E5-2600xx v3 (Haswell-EP) | 18C | 5.69 | 662
 | Broadwell | 14 nm | 4/2016 | E5-26xx v4 (Broadwell-EP) | 22C | 7.2 | 456
Purley | Skylake | 14 nm | 7/2017 | (Skylake-SP) | 28C | n.a. | ~694
Key features of the implementation of Intel’s x86-based “high-end” 2S
server processor lines

## Slide 57: 2.1 Key features of Intel’s major high-end server processor lines (3)
Platform | Core | Techn. | Date of Intro. | High-end multicore 2S server lines | Core count (up to) | L2 cache | L3 cache
 | Pentium 4 DP Presc. | 90 nm | 6/2004 | 90 nm Nocona | 1C | 1 MB | --
 | Pentium 4 Presc. | 90 nm | 10/2005 | Xeon DP 2.8 (Paxville DP) | 2x1C | 2x 2 MB | --
Bensley | Pentium 4 Presc. | 65 nm | 5/2006 | Xeon 50xx (Dempsey) | 2x1C | 2x 2 MB | --
 | Core2 | 65 nm | 6/2006 | Xeon 51xx (Woodcrest) | 2C | 4 MB (shared) | --
 | Core2 | 65 nm | 11/2006 | Xeon 53xx (Clowertown) | 2x2C | 2x 4 MB (shared) | --
 | Penryn | 45 nm | 11/2007 | Xeon 54xx (Harpertown) | 2x2C | 2x 6 MB (shared) | --
Cache architectures of Intel’s high-end 2S SMP server processor lines

## Slide 58: 2.1 Key features of Intel’s major high-end server processor lines (4)
Platform | Core | Techn. | Date of Intro. | High-end multicore 2S server lines | Core count (up to) | L3 cache | No./speed of mem. channels per socket (up to)
 | Pentium 4 Prescott DP | 90 nm | 6/2004 | 90 nm Nocona | 1C | -- | 1x DDR2-400
 | Pentium 4 Prescott 2M DP | 90 nm | 10/2005 | Xeon DP 2.8 (Paxville DP) | 2x1C | -- | 1x DDR2-400
Bensley | Pentium 4 Prescott 2M DP | 65 nm | 5/2006 | Xeon 50xx (Dempsey) | 2x1C | -- | 2x DDR2-667
 | Core2 | 65 nm | 6/2006 | Xeon 51xx (Woodcrest) | 2C | -- | 2x DDR2-667
 | Core2 | 65 nm | 11/2006 | Xeon 53xx (Clowertown) | 2x2C | -- | 2x DDR2-667
 | Penryn | 45 nm | 11/2007 | Xeon 54xx (Harpertown) | 2x2C | -- | 2x DDR2-667
Memory connection of Intel’s high-end 2S SMP server processor lines

## Slide 59: 2.1 Key features of Intel’s major high-end server processor lines (5)
Platform | Core | Techn. | Date of Intro. | High-end multicore 2S server lines | Core count | FSB/QPI (up to) | IF to chipset | PCIe
 | Pentium 4 DP Presc. | 90 nm | 6/2004 | 90 nm Nocona | 1C | 2xFSB 800 MT/s | HI1.5 (266 MB/s) | 24xPCIe (on MCH)
 | Pentium 4 Presc. | 90 nm | 10/2005 | Xeon DP 2.8 (Paxville DP) | 2x1C | 2xFSB 800MT/s | HI1.5 (266 MB/s) | 24xPCIe (on MCH)
Bensley | Pentium 4 Presc. | 65 nm | 5/2006 | Xeon 50xx (Dempsey) | 2x1C | 2xFSB 1066 MT/s | ESI (4xPCIe) | 24xPCIe on MCH
 | Core2 | 65 nm | 6/2006 | Xeon 51xx (Woodcrest) | 2C | 2xFSB 1333 MT/s |  | 
 | Core2 | 65 nm | 11/2006 | Xeon 53xx (Clowertown) | 2x2C | 2xFSB 1066 MT/s |  | 
 | Penryn | 45 nm | 11/2007 | Xeon 54xx (Harpertown) | 2x2C | 2xFSB1033 MT/s |  | 
Interconnection links of Intel’s high-end 2S SMP server processors
Remark: Intel’s client processors provide typically 16 PCIe lanes of the actual gen.

## Slide 60: 2.1 Key features of Intel’s major high-end server processor lines (6)
Platform | Core | Techn. | Date of Intro. | High-end multicore 2S server lines | Chipset | Processor socket
 | Pentium 4 Presc. DP | 90 nm | 6/2004 | 90 nm Nocona | E7520+ ICH5R/6300ESB | mPGA 604
 | Pentium 4 Presc. 2M DP | 90 nm | 10/2005 | Xeon DP 2.8 (Paxville DP) |  | 
Bensley | Pentium 4 Presc. 2M DP | 65 nm | 5/2006 | Xeon 50xx (Dempsey) | 5000+ 631xESB/632xESB | LGA 771
 | Core2 | 65 nm | 6/2006 | Xeon 51xx (Woodcrest) |  | 
 | Core2 | 65 nm | 11/2006 | Xeon 53xx (Clowertown) |  | 
 | Penryn | 45 nm | 11/2007 | Xeon 54xx (Harpertown) |  | 
Chipsets and sockets of Intel’s high-end 2S SMP server platforms

## Slide 61: 2.1 Key features of Intel’s major high-end server processor lines (7)
Platform | Core | Techn. | Date of Intro. | High-end multicore 2S server lines | Core count (up to) | L2 cache/ core | L3 cache/ core
Tylersburg | Nehalem | 45 nm | 3/2009 | Xeon 55xx (Nehalem –EP) Gainestown) | 4C | 256 KB/core | 2 MB/core
Boxboro-EX | Nehalem | 45 nm | 3/2010 | Xeon 65xx Nehalem-EX) | 8C | 256 KB/core | 3 MB/core
 | Westmere | 32 nm | 4/2011 | Xeon E7-28xx (Westmere-EX) | 10C |  | 
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-28xx v2 (Ivy Bridge-EX) | 15C | 256 KB/core | 2.5 MB/core
Grantley | Haswell | 22 nm | 9/2014 | E5-26xx v3 (Haswell-EP) | 18C | 256 KB/core | 2.5 MB/core
 | Broadwell | 14 nm | 4/2016 | E5-26xx v4 (Broadwell-EP) | 22C |  | 
Purley | Skylake | 14 nm | 7/2017 | Silver 41xx (Skylake-SP) | 28C | 1 MB/core | 1.375/core
 | Cascade Lake | 14 nm | 4/2019 | Silver 42xx Cascade Lake-SP | 28C |  | 
?? | Cascade Lake | 14 nm | 4/2019 | Platinum 92xx Cascade Lake-AP | 2x28 | 1 MB/core | 1.375/core
Cache architectures of Intel’s high-end 2S NUMA server processor lines

## Slide 62: 2.1 Key features of Intel’s major high-end server processor lines (8)
Platform | Core | Techn. | Date of Intro. | High-end multicore 2S server lines | Core count (up to) | L3 cache/ core | No./speed of mem. channels per socket (up to)
Tylersburg | Nehalem | 45 nm | 3/2009 | Xeon 55xx (Nehalem –EP) Gainestown) | 4C | 2 MB/core | 3x DDR3-1333
Boxboro-EX | Nehalem | 45 nm | 3/2010 | Xeon 65xx Nehalem-EX) | 8C | 3 MB/core | 8x DDR3-1066
 | Westmere | 32 nm | 4/2011 | Xeon E7-28xx (Westmere-EX) | 10C |  | 8x DDR3-1333
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-28xx v2 (Ivy Bridge-EX) | 15C | 2.5 MB/core | 8x DDR3-1600
Grantley | Haswell | 22 nm | 9/2014 | E5-26xx v3 (Haswell-EP) | 18C | 2.5 MB/core | 4x DDR4-2133
 | Broadwell | 14 nm | 4/2016 | E5-26xx v4 (Broadwell-EP) | 22C |  | 4x DDR4-2400
Purley | Skylake | 14 nm | 7/2017 | Silver 41xx (Skylake-SP) | 28C | 1.375/core | 6x DDR4-2400
 | Cascade Lake | 14 nm | 4/2019 | Silver 42xx Cascade Lake-SP | 28C |  | 6x DDR4-2400
na. | Cascade Lake | 14 nm | 4/2019 | Platinum 92xx Cascade Lake-AP | 2x28 | 1.375/core | 12x DDR4-2933
Memory connection of Intel’s high-end 2S NUMA server processor lines

## Slide 63: 2.1 Key features of Intel’s major high-end server processor lines (9)
Platform | Core | Techn. | Date of Intro. | High-end multicore 2S server lines | Core count | FSB/QPI (up to) | IF to chipset | PCIe
Tylersburg | Nehalem | 45 nm | 3/2009 | Xeon 55xx (Nehalem –EP) Gainestown) | 4C | 2xQPI 1.0 (6.3 GT/s) | QPI 1.0 (6.4 GB/s) | 36x PCIe 2.0 (on MCH)
 | Westmere | 32 nm | 3/2010 | Xeon 56xx (Westmere-EP) | 6C |  |  | 
Boxboro-EX | Nehalem | 45 nm | 3/2010 | Xeon 65xx Nehalem-EX) | 8C | 4xQPI 1.0 (6.4 GT/s) | 2xQPI 1.0 (6.4 GT/s) | 36x PCIe 2.0 (on MCH)
 | Westmere | 32 nm | 4/2011 | Xeon E7-28xx (Westmere-EX) | 10C |  |  | 
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-28xx v2 (Ivy Bridge-EX) | 15C | 3xQPI 1.1 (8 GT/s) | DMI2 x4 (4xPCIe 2.0) (2 GB/s Perdir.) | 32x PCIe 3.0 (on proc.)
Grantley | Haswell | 22 nm | 9/2014 | E5-26xx v3 (Haswell-EP) | 18C | 2xQPI 1.1 (8 GT/s) | DMI2 x4 (4xPCIe 2.0) (2 GB/s Per dir.) | 40x PCIe 3.0 (on proc.)
 | Broadwell | 14 nm | 4/2016 | E5-26xx v4 (Broadwell-EP) | 22C |  |  | 
Purley | Skylake | 14 nm | 7/2017 | Silver 41xx (Skylake-SP) | 12C | 2x UPI (9.6 GT/s) | DMI3 x4 (4xPCIe 3.0) (4 GB/s per dir.) | 44/48x PCIe 3.0 (on proc.)
 | Cascade Lake | 14 | 4/2019 | Silver 42xx Cascade Lake-SP | 16C | 2x UPI (10.4 GT/s) |  | 
?? | Cascade Lake | 14 | 4/2019 | Platinum 92xx Cascade Lake-AP | 2x28C | na. | na. | na.
Interconnection links of Intel’s high-end 2S NUMA server processors

## Slide 64: 2.1 Key features of Intel’s major high-end server processor lines (10)
Platform | Core | Techn. | Date of Intro. | High-end multicore 2S server lines | Chipset | Processor socket
Tylersburg | Nehalem | 45 nm | 3/2009 | Xeon 55xx (Nehalem –EP) Gainestown) | 55xx+ ICH9/ICH10 | LGA 1366
Boxboro-EX | Nehalem | 45 nm | 3/2010 | Xeon 65xx Nehalem-EX) | 75xx+ ICH10 | LGA 1567
 | Westmere | 32 nm | 4/2011 | Xeon E7-28xx (Westmere-EX) |  | 
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-28xx v2 (Ivy Bridge-EX) | C602 (Pattsburg) | LGA 2011-1
Grantley | Haswell | 22 nm | 9/2014 | E5-26xx v3 (Haswell-EP) | C612 (Wellsburg) | LGA 2011-3
 | Broadwell | 14 nm | 4/2016 | E5-26xx v4 (Broadwell-EP) |  | 
Purley | Skylake | 14 nm | 7/2017 | Silver 41xx (Skylake-SP) | C621/C622 (Lewisburg) | LGA 3647
 | Cascade Lake | 14 | 4/2019 | Silver 42xx Cascade Lake-SP |  | 
?? | Cascade Lake | 14 | 4/2019 | Platinum 92xx Cascade Lake-AP |  | BGA 5903
Chipsets and sockets of Intel’s high-end 2S NUMA server platforms

## Slide 65: 2.1 Key features of Intel’s major high-end server processor lines (11)
Platform | Platform topology | Date of intro. | Processor | Techn. | Core count (up to) | L3 cache (up to) | No. and max. speed of memory channels/proc. socket | Kind of connecting memory to the MCs
Truland MP | SMP w/dual FSBs | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 90 nm | 1C | 8 MB | 2x DDR2-400/socket | 4 low line count serial channels (IMI) with on-board mem. buffers, 2 DIMM channels/ mem. buffer (MCs in the MCH) LGA 604
 |  | 11/2005 | Xeon 7000 (P4) (Paxville MP) | 90 nm | 2x1C | -- |  | 
 |  | 8/2006 | Xeon 7100 (P4) (Tulsa) | 65 nm | 2C | 16 MB |  | 
Caneland | SMP w/Quad FSBs | 9/2007 | Xeon 7200 (Core 2) Tigerton DC | 65 nm | 2C | -- | 1x DDR2-667/socket (FB-DIMM) | 4 low line count serial FB-DIMM channels (IMI2) with on-DIMM mem. buffers (MCs in the MCH) LGA 604
 |  | 9/2007 | Xeon 7300 (Core 2) Tigerton QC | 65 nm | 2x2C | -- |  | 
 |  | 9/2008 | Xeon 7400 (Penryn) (Dunnington) | 45 nm | 6C | 16 MB |  | 
Memory connection of Intel’s high-end 4S SMP server processor lines

## Slide 66: 2.1 Key features of Intel’s major high-end server processor lines (12)
Platform/ Scalability | Processor core | Techn. | Intro. | High-end 4S/8S server processor lines | Core count | Chipset | Proc. socket
Truland MP (4S) | Pentium 4 MP Prescott | 90 nm | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 1C | E8500 + ICH5 | LGA 604
 | Pentium 4 Presc. | 90 nm | 11/2005 | 7000 (Paxville MP) | 2x1C | E8501 + ICH5 | 
 | Pentium 4 Presc. | 65 nm | 8/2006 | 7100 (Tulsa) | 2x1C |  | 
Caneland (4S) | Core2 | 65 nm | 9/2007 | 7200 (Tigerton DC) 7300 (Tigerton QC) | 2C 2x2C | E7300 (Clarksboro)+ 631x/632x ESB | LGA 604
 | Penryn | 45 nm | 9/2008 | 7400 (Dunnington) | 6C |  | 
Chipsets and sockets of Intel’s high-end 4S SMP server platforms

## Slide 67: 2.1 Key features of Intel’s major high-end server processor lines (13)
Platform | Platform topology | Date of intro. | Processor | Techn. | Core count (up to) | L3 cache (up to) | No. and max. speed of memory channels/proc. socket | Kind of connecting memory to the MCs
Boxboro-EX | NUMA, fully connected for 4S platforms, partially connected for 8S platforms | 3/2010 | Nehalem-EX (Xeon 7500/ (Beckton) | 45 nm | 8C | 8x3 MB | 8x DDR3-1067/socket | 4 low line count serial channels (SMI) on-board mem. buffers, 2 DIMM channels (MCs on the proc. die) LGA 1567
 |  | 4/2011 | Westmere-EX (E7-8800) | 32 nm | 10C | 10x3 MB |  | 
Brickland |  | 2/2014 | Ivy Bridge-EX (E7-8800 v2) | 22 nm | 15C | 15x2.5 MB | 8x DDR3-1600/socket | 4 low line count serial channels (SMI2) with on-board mem. buffers, 2 DIMM channels/mem. buffer (MCs on the proc. die) LGA-2011-1
 |  | 5/2015 | Haswell-EX (E7-8800 v3) | 22 nm | 18C | 18x2.5 MB | 8x DDR4-1866/socket | 
 |  | 6/2016 | Broadwell-EX (E7-8800 v4) | 14 nm | 24C | 24x2.5 MB | 8x DDR4-1866/socket | 
Purley |  | 7/2017 | Skylake-SP (Platinum 8100) | 14 nm | 28C | 28x2.5 MB | 6x DDR4-2666/socket | 6 direct attached DDR4 channels LGA-3647
Memory connection of Intel’s high-end 4S NUMA server processor lines

## Slide 68: 2.1 Key features of Intel’s major high-end server processor lines (14)
Platform/ Scalability | Processor core | Techn. | Intro. | High-end 4S/8S server processor lines | Core count | Chipset | Proc. socket
Boxboro-EX (8S) | Nehalem | 45 nm | 3/2010 | 7500 (Beckton/ Nehalem-EX) | 8C | 7500 (Boxboro) + ICH10 | LGA 1567
 | Westmere | 32 nm | 4/2011 | E7-8800 (Westmere-EX) | 10C |  | 
 | Sandy Bidge | 32 nm |  |  |  |  | 
Brickland (8S) | Ivy Bridge | 22 nm | 2/2014 | E7-8800 v2 (Ivy Bridge-EX) | 15C | C602J (Patsburg J) | LGA 2011-1
 | Haswell | 22 nm | 5/2015 | E7-8800 v3 (Haswell-EX) | 18C |  | 
 | Broadwell | 14 nm | 6/2016 | E7-8800 v4 (Broadwell-EX) | 24C |  | 
Purley (2S/4S/8S) | Skylake | 14 nm | 7/2017 | Platinum 8100 (Skylake-SP) | 28C | C620 (Lewisburg) | LGA 3647
 | Cascade Lake | 14 nm | 4/2019 | Platinum 8200 (Cascade Lake-SP) | 28C |  | 
Chipsets and sockets of Intel’s high-end 4S NUMA server platforms

## Slide 69
2.2 Evolution of core counts and memory speeds in Intel’s
major server processor lines
Notes: 69

## Slide 70: 2.2 Evolution of core counts and memory speeds in Intel’s server lines (1)
Evolution of core counts and memory speeds in Intel’s major server
processor lines
In this Section, subsequently we cover Intel’s 2S and 4S/8S high-end server
processor lines and the rate of rising memory speeds in Intel’s DT and 2S server
lines.

## Slide 71: 2.2 Evolution of core counts and memory speeds in Intel’s server lines (2)
Rising core counts in Intel's high-end 2S server processor lines
Core count
2006
2008
2010
2012
2014
2016
Year
DP 2.8 GHz
(90 nm)
53xx
(65 nm)
54xx
(45 nm)
Nehalem-EX
(45 nm)
Westmere-EX
(32 nm)
Ivy-Bridge-EX
(22 nm)
Broadwell-EP
(14 nm)
*
*
*
*
*
2
4
8
18
28
24
10
6
15
*
*
~2x/4 years
~2x/2 years
Emergence of
L3 caches in the
Core 2-based DP line
*
Haswell-EP
(22 nm)
Skylake-SP
(14 nm)
*
51xx
(65 nm
*
Two-die
implementations
12
2018
56
*
Cascade Lake-AP
(14 nm, 2 dies)
*
*
Cascade Lake-SP
(14 nm)
*
55xx
(Nehalem-EP)
(45 nm)
64
32
*

## Slide 72: 2.2 Evolution of core counts and memory speeds in Intel’s server lines (3)
Core count
2006
2008
2010
2012
2014
2016
Year
DP 2.8 GHz
(90 nm)
53xx
(65 nm)
54xx
(45 nm)
Nehalem-EX
(45 nm, 2461 $)
Westmere-EX
(32 nm, 4227 $)
Ivy-Bridge-EX
(22 nm, 6451 $)
Broadwell-EP
(14 nm, 4938 $)
*
*
*
*
*
2
4
8
18
28
24
10
6
15
*
*
~2x/4 years
~2x/2 years
Emergence of
L3 caches in the
Core 2-based DP line
*
Haswell-EP
(22 nm, 4115 )
Skylake-SP
(14 nm, 1112 $)
*
51xx
(65 nm
*
Two-die
implementations
12
2018
56
*
Cascade Lake-AP
(14 nm, 2 dies, na.)
*
*
Cascade Lake-SP
(14 nm, 1002 $)
Lower core counts than
enabled by technology
due to business considerations
Higher core counts due to
dual dies
AMD
EPYC
(8-32C)
AMD
EPYC2
(64C)
*
55xx
(Nehalem-EP)
(45 nm, 1600 $)
Rising core counts in Intel's high-end 2S server processor lines with price
quotations
*
*
32
64
(2100 $)
(6950 $)
*

## Slide 73: 2.2 Evolution of core counts and memory speeds in Intel’s server lines (4)
Rising core counts in Intel’s high-end 4S server processor lines
Core count
2006
2008
2010
2012
2014
2016
Year
7000
(90 nm)
7300
(65 nm)
7400
(45 nm)
Nehalem-EX
(45 nm)
Westmere-EX
(32 nm)
Ivy-Bridge-EX
(22 nm)
Broadwell-EX
(14 nm)
*
*
*
*
*
2
4
8
18
28
24
10
6
15
*
*
~2x/4 years
~2x/2 years
Emergence of
L3 caches
in the Core 2 line
*
*
Haswell-EX
(22 nm)
Skylake-SP
(14 nm)
*
7100
(65 nm
16 MB L3)
*

## Slide 74
2.2 Evolution of core counts and memory speeds in Intel’s server lines (5)
Transfer rate (MT/s)
50
100
500
Year
05
2004
06
07
08
1000
3000
200
2000
~ 2*/4 years
09
11
2010
12
13
15
DDR3
1067

14
~ 2*/8 years
x
x
x
x
DDR
400
DDR2
667
DDR3
1600
2S
Emergence of
DDR3 memory
16
17
x
DDR4
2400
DDR4
2933
Emergence of
DDR4 memory
Evolution of memory transfer rates in Intel’s high-end 2S server processors
*
19
18
2020
DDR3
1333
x
x
x
DDR4
2666
DDR4
3200
x
AMD
EPYC
AMD
EPYC 2G

## Slide 75
2.2 Evolution of core counts and memory speeds in Intel’s server lines (6)
*
Transfer rate (MT/s)
50
100
500
Year
03
05
01
02
04
06
07
08
1000
3000
200
2000
~ 2*/4 years
DDR2
533
DDR2
667
DDR2 800
DDR3
1600
09
11
2010
12
13
15
DDR3
1067
2000

14
*
DDR3
1333
DDR3/1866
*
DDR
333
~ 2*/8 years
DDR
266
x
x
x
x
*
DDR
400
DDR2
667
DDR3
1600
DDR3/4
1866
DDR
400
DDR3
1067
DTs
4S/8S
Emergence of
DDR3 memory
16
17
*
*
*
*
*
*
x
x
DDR4
1866
DDR4
2666
Emergence of
DDR4 memory
*
*
DDR4/2133
x
DDR4/2400
Evolution of memory transfer rates in Intel’s DTs and HE 4S/8S servers
HE: High-End
*

## Slide 76
3. The memory bandwidth obstacle of server platforms
3.1 Consequences of slower dynamics of memory rates
vs. core counts in server lines
3.2 Addressing the threat of a memory bandwidth bottleneck
3.3 Constrains for raising the number of direct connected
standard DRAM channels to the MCH or a processor
3.4 Design space of connecting memory subsystems to
server platforms
Notes: 76

## Slide 77
3.1 Consequences of slower dynamics of memory rates vs. core counts in server lines
Notes: 77

## Slide 78: 3.1 Consequences of slower dynamics of memory rates vs. core counts (1)
3.1 Consequences of slower dynamics of memory rates vs. core counts
in multicore servers
Both in Intel’s 2S and 4S server processors but also in AMD’s previous Bulldozer
based processor lines memory speeds has been raised slower than core counts
[46].
What would happen when generation over generation memory speeds raise slower
than core counts whereas the number of memory channals would remain
the same?
BWM/core = nM ∗ w ∗ TM /nC
with nM: Number of memory channels
w: Width of a memory channel (8 byte)
TM: Transfer rate of the memory (e.g 2.4 GT/s)
nC: Core count
The per core memory bandwidth of a socket (BWM/core) amounts to
If in subsequent processor generations the memory transfer rate (TM) raises
slower than the core count (nC), the expression TM/nC and along with it
the per core memory bandwidth (BWM/core) becomes smaller according to the
expression
Consequently, a memory bandwidth gap would emerge without raising the
number of memory channels.
BWM/core = nM ∗ w ∗ TM /nC
*

## Slide 79
3.2 Addressing the threat of memory bandwidth bottleneck
Notes: 79

## Slide 80: 3.2 Addressing the threat of a memory bandwidth bottleneck (1)
3.2 Addressing the threat of a memory bandwidth bottleneck
In a multicore processor every core may run independently from each other,
consequently, while processor generations evolve
the per core memory bandwidth should be preserved, in other words ,
the memory bandwidth needs to be linearly scaled with the core count.
BWM/core = nM ∗ w ∗ TM /nC
While the ratio of TM /nC decreases, the per-core memory bandwidth (BWM/core)
may be preserved if nM will suitable be increased, as the expression for
BWM/core reveals:
In other words
nM ∗ TM/nC should remain constant while nC increases.
Here we assume that the width of the memory channels (w) remains unchanged
and the intended application domain remains unchanged.
i.e.
while a processor family evolves generations over generations and core counts
rise in a higher rate than memory speeds, the resulting per core memory
bandwidth deficit should be compensated by appropriately increasing the
number of memory channels (nM) of the platform.
*

## Slide 81: 3.2 Addressing the threat of a memory bandwidth gap (2)
The number of memory channels (nM) needed per socket for preserving the
per core memory bandwidth of an n-core high-end 4S/8S server
nC | nM
2 | 2.0
4 | 2.8
6 | 3.5
8 | 4.0
10 | 4.5
12 | 4.9
14 | 5.3
16 | 5.6
20 | 6.3
24 | 6.9
32 | 8.0
48 | 9.8
64 | 11.3
It has been shown [46] that for the assumed evolution rates of core counts and memory speeds a high-end server with nC cores needs approximately
nM = √2 ∗ √n memory channels per socket if the per core memory bandwidth
should be preserved related to a chosen previous single core 2S server
implementation (Nocona).
Table: The number of memory channels (nM)
needed per socket for preserving the per core
memory bandwidth of a high-end server with
nC cores related to a selected previous platform.
*
The required memory channel numbers per socket
(nC) are shown in the Table on the right.

## Slide 82: 3.2 Addressing the threat of a memory bandwidth gap (3)
Providing enough memory channels and thus memory bandwidth per socket is
one of the key challenges in designing server processors and platforms since
multicores emerged and core counts continuously raise at a higher rate than
memory speeds , as electrical and power issues constrain the expansion of
memory channels, as discussed in the subsequent Sections.
The driving force of the evolution of memory subsystems in servers

## Slide 83: 3.2 Addressing the threat of a memory bandwidth gap (4)
In order to preserve the per core memory bandwidth the number of memory
channels rose rapidly from 1 per socket to 12 per socket in Intel's high-end 2S
server platforms, as shown in the next Tables.
Example: Raising the number of memory channels (nM) in Intel's high-end
2S servers
*

## Slide 84: 3.2 Addressing the threat of a memory bandwidth gap (5)
Platform | Core | Techn. | Date of Intro. | High-end multicore 2S server lines | Core count (up to) | L3 cache | No./speed of mem. channels per socket (up to)
 | Pentium 4 MP Presc. | 90 nm | 6/2004 | 90 nm Nocona | 1C | -- | 1x DDR2-400
 | Pentium 4 Presc. | 90 nm | 10/2005 | Xeon DP 2.8 (Paxville DP) | 2x1C | -- | 1x DDR2-400
Bensley | Pentium 4 Presc. | 65 nm | 5/2006 | Xeon 50xx (Dempsey) | 2x1C | -- | 2x DDR2-667
 | Core2 | 65 nm | 6/2006 | Xeon 51xx (Woodcrest) | 2C | -- | 2x DDR2-667
 | Core2 | 65 nm | 11/2006 | Xeon 53xx (Clowertown) | 2x2C | -- | 2x DDR2-667
 | Penryn | 45 nm | 11/2007 | Xeon 54xx (Harpertown) | 2x2C | -- | 2x DDR2-667
Number of memory channels per socket in Intel’s high-end 2S SMP server
platforms

## Slide 85: 3.2 Addressing the threat of a memory bandwidth gap (6)
Platform | Core | Techn. | Date of Intro. | High-end multicore 2S server lines | Core count (up to) | L3 cache/ core | No./speed of mem. channels per socket (up to)
Tylersburg | Nehalem | 45 nm | 3/2009 | Xeon 55xx (Nehalem –EP) Gainestown) | 4C | 2 MB/core | 3x DDR3-1333
Boxboro-EX | Nehalem | 45 nm | 3/2010 | Xeon 65xx Nehalem-EX) | 8C | 3 MB/core | 8x DDR3-1066
 | Westmere | 32 nm | 4/2011 | Xeon E7-28xx (Westmere-EX) | 10C |  | 8x DDR3-1333
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-28xx v2 (Ivy Bridge-EX) | 15C | 2.5 MB/core | 8x DDR3-1600
Grantley | Haswell | 22 nm | 9/2014 | E5-26xx v3 (Haswell-EP) | 18C | 2.5 MB/core | 4x DDR4-2133
 | Broadwell | 14 nm | 4/2016 | E5-26xx v4 (Broadwell-EP) | 22C |  | 4x DDR4-2400
Purley | Skylake | 14 nm | 7/2017 | Silver 41xx (Skylake-SP) | 28C | 1.375/core | 6x DDR4-2400
 | Cascade Lake | 14 nm | 4/2019 | Silver 42xx Cascade Lake-SP | 28C |  | 6x DDR4-2400
?? | Cascade Lake | 14 nm | 4/2019 | Platinum 92xx Cascade Lake-AP | 2x28 | 1.375/core | 12x DDR4-2933
Number of memory channels per socket in Intel’s high-end 2S NUMA server
platforms

## Slide 86: 3.2 Addressing the threat of a memory bandwidth gap (7)
Relative per core bandwidth in Intel’s 2S server platforms -1
Let’s take Intel’s early single-core Nocona-based platform as a reference platform
and let’s calculate the per core memory bandwidth provided by the enlisted
high-end 2S platforms (see next Table).

## Slide 87: 3.2 Addressing the threat of a memory bandwidth gap (8)
Platform | Core | Techn. | Date of Intro. | High-end multicore 2S server lines | Core count (up to) | No./speed of mem. channels per socket (up to) | Scaled nM per socket | Per core BW rel. to ref. platform
Reference platform | Pentium 4 Prescott DP | 90 nm | 6/2004 | 90 nm Nocona | 1C | 1x DDR2/400 | 1.0 | 1.0
 | Pentium 4 Presc. | 90 nm | 10/2005 | Xeon DP 2.8 (Paxville DP) | 2x1C | 1x DDR2/400 | 1.4 | 0.5
Bensley | Pentium 4 Presc. | 65 nm | 5/2006 | Xeon 5000 (Dempsey) | 2x1C | 2x DDR2/667 | 1.4 | 1.7
 | Core2 | 65 nm | 6/2006 | Xeon 5100 (Woodcrest) | 2C | 2x DDR2/667 | 1.4 | 1.7
 | Core2 | 65 nm | 11/2006 | Xeon 5300 (Clowertown) | 2x2C | 2x DDR2/667 | 2.0 | 0.8
 | Penryn | 45 nm | 11/2007 | Xeon 5400 (Harpertown) | 2x2C | 2x DDR2/667 | 2.0 | 0.8
Tylersburg | Nehalem | 45 nm | 3/2009 | Xeon 55xx (Gainestown) | 4C | 3x DDR3/1333 | 2.0 | 2.5
Boxboro-EX | Nehalem | 45 nm | 3/2010 | Xeon X6500 Nehalem-EX) | 8C | 8x DDR3/1066 | 2.8 | 2.7
 | Westmere | 32 nm | 4/2011 | Xeon E7-28xx (Westmere-EX) | 10C | 8x DDR3/1333 | 3.2 | 2.7
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-28xx v2 (Ivy Bridge-EX) | 15C | 8x DDR3/1600 | 3.9 | 2.1
Grantley | Haswell | 22 nm | 9/2014 | E5-2600xx v3 (Haswell-EP) | 18C | 4x DDR4/2133 | 4.2 | 1.2
 | Broadwell | 14 nm | 4/2016 | E5-26xx v4 (Broadwell-EP) | 22C | 4x DDR4/2400 | 4.7 | 1.1
Purley | Skylake | 14 nm | 7/2017 | Silver 41xx Skylake-SP) | 28C | 6x DDR4/2400 | 5.3 | 1.3
 | Cascade Lake | 14 nm | 4/2019 | Silver 41xx Skylake-SP) | 28C | 6x DDR4/2933 | 5.3 | 1.6
Relative per core bandwidth in Intel’s 2S server platforms -2

## Slide 88: 3.2 Addressing the threat of a memory bandwidth gap (9)
Relative per core bandwidth in Intel’s 2S server platforms -3
Data in the last but one column shows the number of memory channels needed
for the same per-core memory bandwidth as provided by the reference platform
whereas the last column (Per core BW rel. to ref. platform) provides a comparison
about the actual bandwidth of the discussed platform relative to the reference
platform.
It can be stated that over generation the relative memory bandwidth remained
about the same mainly with the exception of the platforms with low line count
serial and parallel interfaces (Nehalem/Westmere-based server platforms).
In these platforms Intel provided 2.5 – 2.7 times higher bandwidth than the
reference platform but this was corrected it in their subsequent direct attached
designs (beginning with the Haswell-based platform).
*

## Slide 89
3.3 Constrains for raising the number of direct connected standard DRAM channels to the MCH or a processor
Notes: 89

## Slide 90: 3.3 Constrains for raising the number of direct connected DRAM channels (1)
3.3 Constraints for raising the number of directly connected standard
DRAM channels to the MCH or a processor -1
In early server and client platforms memory channels were typically directly
connected to the MCH, also recent client and server platforms attach memory
usually directly to the processor or processors, as the examples below illustrate it.
Xeon MP1
SC
FSB
Xeon MP1
SC
ICH
MCH
E.g. HI 1.5
HI 1.5 266 MB/s
E.g. PC800 RDRAM
E.g. 400 MT/s
Pentium 4 Willamette
With SMP support
(called Foster) (2001)
Core 2 7th generation
(Skylake based DP server)
(2017)
PCH
(Z170)
E.g. DDR4-2400
PCIe3 x16
High-level block diagram of an
early Pentium 4 based DP server
High-level block diagram of a
recent Core 2 Skylake based DP server
PCIe
Core I7
7. Gen.
*

## Slide 91: 3.3 Constrains for raising the number of direct connected DRAM channels (2)
Constraints for raising the number of directly connected standard
DRAM channels to the MCH or a processor -2
For directly connected standard DIMM channels each memory channel requires
a large number of copper traces since these interconnects are parallel, 8-byte
wide links.
The exact number of copper traces needed depends on the memory type used,
for actual numbers see the next Figure.
*

## Slide 92: 3.3 Constrains for raising the number of direct connected DRAM channels (3)
All DIMMs
are 8-byte wide.
Pin counts of SDRAM
to DDR4 DIMMs
SDRAM
(SDR)
DDR
DDR2
DDR3
168-pin
184-pin
240- pin
240-pin
DDR4
284-pin
2.1 Overview of the Truland MP platform (1)
*
Notes: 92

## Slide 93: 3.3 Constrains for raising the number of direct connected DRAM channels (4)
The interconnects between the MCH or the processor socket and the DIMM
socket(s) are implemented by dense copper trails on the mainboard, as seen
below, typically equalized to reduce skews (differences in signal propagation times
occurring on different long bit-lines).
Figure: Copper trails between the MCH or processor socket and the DIMM socket(s)
Constraints for raising the number of directly connected standard
DRAM channels to the MCH or a processor -3

## Slide 94: 3.3 Constrains for raising the number of direct connected DRAM channels (5)
For directly connected memory channels electrical constrains impose a hard limit
on the maximum number of attachable memory channels.
This limitation arises mainly from the fact that width and distance of copper trails
from each other determine their electrical parameters and thus the temporal
behavior of the interconnect, first of all its maximum transfer rate, as we
discuss subsequently.
Constraints for raising the number of directly connected standard
DRAM channels to the MCH or a processor -4
*

## Slide 95: 3.3 Constrains for raising the number of direct connected DRAM channels (6)
For Vin = 1V:
The temporal behavior of signals on DIMM traces can be modelled by a serial RC
circuit with R representing the ohmic impedance and C the capacitance of a trace,
as shown below.
Figure: The circuit model and the related expression for Vc [12]
Modelling the temporal behavior of dense copper traces interconnecting
the MCH or the processor and the DIMMs

## Slide 96: 3.3 Constrains for raising the number of direct connected DRAM channels (7)
Vc
(Vin = 1 V)
Raising the voltage on a capacitor of a serial RC network that models
DIMM trails
= R * C

## Slide 97: 3.3 Constrains for raising the number of direct connected DRAM channels (8)
What happens if the number of direct attached memory channels would be doubled?
MCH or processor socket
MCH or processor socket
,
More memory channels would require more cupper traces to attach to the socket,
this could only be implemented with smaller and denser cupper traces, then
however R and C and thus τ of the cupper traces would be increased, as illustrated
in the Figure below.

## Slide 98: 3.3 Constrains for raising the number of direct connected DRAM channels (9)
Raising the voltage on a capacitor of a serial RC circuit that models DIMM
trails when τ is doubled
Vc
(Vin = 1 V)
= R * C
Longer rise and fall times, however would reduce the feasible memory transfer rate.

## Slide 99: 3.3 Constrains for raising the number of direct connected DRAM channels (10)
If however, would be raised the given memory speed grade (e.g. DDR4-2400)
could not be preserved.
In other words, a given memory speed grade constrains the number and
width of the copper trails that can be connected to an MCH or processor socket
width a given width and thus it limits the number of memory channels that
may directly be connected to an MCH or a processor.
In this respect the physical dimensions of the MCH or processor socket are
of paramount importance since larger sockets allow obviously, more copper
trails to connect whereas smaller sockets less copper trails and thus more or
less memory channels.
On the other hand, larger processor sockets enable connecting more memory channels, say up to 6 channels directly, as the next Figure indicates.
Usual MCH or client processor sockets of about 30 - 40 mm x 30 – 40 mm)
allow typically to connect up to two memory channels directly to an MCH or a
processor socket without degrading memory speed.
Constraints for raising the number of directly connected standard
DRAM channels to the MCH or a processor -5
*

## Slide 100: 3.3 Constrains for raising the number of direct connected DRAM channels (11)
34x34 mm
45x42.5 mm
58.5x51.0 mm
76x56 mm
BGA 1226
LGA 1366
LGA 2011-3
LGA 3647
2xDDR2 standard
mem. channels
on MCH
3xDDR3 standard
mem. channels
on processors
2x2 DDR4 standard
mem. channels
(2 on both side)
2x3 DDR4 standard
mem. channels
(3 on both side)
P965 GMCH
for Core 2
(2 cores)
Westmere-EP
(up to 6 cores)
Broadwell-EP
(up to 22 cores)
Skylake-SP
(up to 28 cores)
Note: Physical/electrical constraints limit the number of attachable memory channels
Source of the pictures [13]
Socket sizes and number of directly attached memory channels to Intel’s
processors

## Slide 101
3.4 Design space of connecting memory subsystems to server platforms
Notes: 101

## Slide 102: 3.4 Design space of connecting memory subsystems to server platforms (1)
As pointed out in Section 2.2 memory transfer rates rise in high-end 2S or 4S/8S
servers slower than core counts and thus a memory bandwidth bottleneck
arises unless appropriately more memory channels do not compensate it.
This is however, an intricate task since the number of directly attachable
memory channels to an MCH or processor is restricted due to physical and
electrical constraints, as discussed before e.g. more or less to two if memory
channels are connected via MCHs or client processors of typical package sizes
(of about 30 – 40 x 30 - 40 mm).
This Section is devoted entirely to this point by discussing the design space
utilized for increasing the number of memory channels in server platforms
to compensate slower raising memory speeds comperad to core counts.
3.4 Design space of connecting memory subsystems to server platforms
*

## Slide 103: 3.4 Design space of connecting memory subsystems to server platforms (2)
Where to connect DIMMs
to the server platform?
How to connect
DIMMs to the MCs?
Connecting memory subsystems to server platforms
Design space of connecting memory subsystems to server platforms
There are two main aspects for connecting memory i.e. DIMMs to a server platform,
as shown below.
MC: Memory Controller
*

## Slide 104: 3.4 Design space of connecting memory subsystems to server platforms (3)
Where to connect DIMMs
to the server platform?
DIMMs are connected to a single point
of the platform.
This may cause severe bandwidth imitations
in multiprocessors.
Connecting DIMMs
to the MCH (Memory Control Hub)
(yielding SMPs)
Memory
Processor
MCH
Processor
a) Where to connect DIMMs to the server platforms?
DIMMs are connected per processor, i.e. distributed.
This provides an inherent scaling
of memory channels with the processor count,
i.e. the number of memory channels
raises linearly with the processor count
in multiprocessors.
Connecting DIMMs directly
to the processors
(yielding NUMAs)
MCH
Processor
Processor
*

## Slide 105: 3.4 Design space of connecting memory subsystems to server platforms (4)
Montecito (2C) (2006)
Opteron server lines (1C) (2003)
Opteron server lines (2C) 2005)
and all subsequent AMD lines
PA-8800 (2004)
PA-8900 (2005)
and all previous PA lines
Core 2 Duo line (2C) (2006)
and all preceding Intel lines
Core 2 Quad line (2x2C) (2006/2007)
Penryn line (2x2C) (2008)
Nehalem lines (4) (2008)
and all subsequent Intel lines
Tukwila (4C) (2010)
AMD’s K7 lines (1C)
(1999-2003)
UltraSPARC III (1C) (2001)
and all subsequent Sun lines
UltraSPARC II (1C) (~1997)
Connection point of memory
Connecting memory to the processor(s)
(NUMA)
Connecting DIMMs to the MCH
(SMP)
Transition of the connection point of DIMMs in the evolution of processors
POWER1 (RS/6000) (1990)
direct connection via external circuitry
since POWER5 (2C) (2005)
on-die integrated mem. controller

## Slide 106: 3.4 Design space of connecting memory subsystems to server platforms (5)
How to connect DIMMs to the MCs?
Connecting DIMMs
via standard DRAM interfaces
directly to the MCs
DIMMs are connected to one or more memory controllers (MCs) directly by standard DRAM interfaces.
Standard DRAM
interface
DIMMs
MC in
MCH or processor
b) How to connect DIMMs to the MCs?
Connecting DIMMs
via low-line-count links and
memory buffers (MBs) to the MCs
DIMMs are connected to one or more
memory controllers (MCs) via low-line-count interfaces and interface converters, called
memory buffers (MBs).
MB
MB
Standard DRAM
interface
Low line count
interface
DIMMs
Figure: Options for implementing the connection path between the MCs and the DIMMs
Memory
Buffers
This option allows to connect more memory channels
than feasible by using standard DRAM memory interfaces
but the MBs incur additional delay and power consumption.
*
MB
MC in
MCH or processor
(No. of mem. channels
depends on socket size)

## Slide 107: 3.4 Design space of connecting memory subsystems to server platforms (6)
Using low-line-count parallel links to connect MBs to the MCs
Connecting DIMMs via low-line-count links and memory buffers (MBs) to the MCs
Using low-line-count serial links to connect MBs to the MCs
b2) Connecting DIMMs via low line count links and memory buffers (MBs)
to the MCs -1
There are two basic options for implementing low-line count links:
MB
MB
Standard DRAM
interface
Low line count
serial interface
DIMMs
Memory
Buffers
*
MB
MC in
MCH or processor
MB
MB
Standard DRAM
interface
Low line count
parallel interface
DIMMs
Memory
Buffers
MB
MC in
MCH or processor
Figure: Options for using serial or parallel connection path between the MCs and the MBs

## Slide 108: 3.4 Design space of connecting memory subsystems to server platforms (7)
Using low-line-count parallel links to connect MBs to the MCs
Connecting DIMMs via low-line-count links and memory buffers (MBs) to the MCs
The links are implemented as
64-bit parallel, bidirectional channels
typically with single-ended voltage reference signaling, termed as VMSE
(Voltage Mode Single Ended) signaling
a) Using low-line-count serial links to connect MBs to the MCs -1
Using low-line-count serial links to connect MBs to the MCs
Figure: Example for differential signaling [2]
The links are implemented as
two unidirectional, Point-to-Point serial,
packet based channels,
typically with differential signaling.
Benefit: No need for
serial/parallel conversion
in the MBs, only interface conversion is required
Implemented links (IMI, SMI) have about 70 lines
(vs. 240 for DDR2/3).
Drawback: The MBs have to perform
serial/parallel conversion,
this increases delay and dissipation.
Intel's implementation (the SMI 2 interface)
comprises about 110 lines.
*

## Slide 109
LVDS: Low Voltage Differential Signaling LVTTL: Low Voltage TTL
(D)RSL: (Differential) Rambus Signaling Level SSTL: Stub Series Terminated Logic VCM: Common Mode Voltage VREF: Reference Voltage
VMSE: Voltage Mode Single Ended FB-DIMM: Fully Buffered DIMM
LVTTL (3.3 V)
FPM/EDO
SDRAM
HI 1.5
TTL (5 V)
FPM/EDO
SSTL
SSTL2 (DDR)
SSTL1.8 (DDR2)
SSTL1.5 (DDR3)
SSTL1.2 (DDR4)
RSL (RDRAM)
FSB
VMSE (SMI2)
LVDS
PCIe
QPI, DMI, ESI
FB-DIMMs
DRSL
XDR (data)
FB-DIMM
IMI, SMI
Use of serial differencial or parallel VMSE signals to interconnect MCs and MBs
3.4 Design space of connecting memory subsystems to server platforms (8)
Signals
Single ended
voltage referenced
Single ended
ground referenced
Differential
t
t
VREF
t
S+
S-
VCM
Typ.voltage
swings
600-800 mV
200-300 mV
3.3-5 V
Signaling
system
used in
*

## Slide 110: 3.4 Design space of connecting memory subsystems to server platforms (9)
While using low-line-count serial links where to place MBs?
Placing MBs on-DIMMs
(FB-DIMMs)
The FB-DIMMs are DDR2 based.
The MBs are placed directly
on DIMMs as part of FB-DIMMs
Placing MBs on-board
(on mainboard/riser card)
The MBs are placed on the mainboard or riser cards
While using low line count serial links where to place memory buffers (MBs)?
*
On-board MB
PCH
Pentium 4 based Truland MP server board
(2006) [14]
FB-DIMM based memory subsystem [15]

## Slide 111: 3.4 Design space of connecting memory subsystems to server platforms (10)
b) Using low-line-count parallel links to connect MBs to the MCs
The links are implemented as 64-bit parallel, bidirectional channels typically
with single-ended voltage reference signaling, termed VMSE (Voltage Mode
Single Ended) signaling.
Benefit: No need for serial/parallel conversion in the MBs, only interface
conversion is needed? this reduces dissipation.
Intel's implementation (the SMI 2 interface) comprises about 110 lines.
Memory buffers (MB) are placed on the mainboard.
*

## Slide 112: 3.4 Design space of connecting memory subsystems to server platforms (11)
The resulting design space of implementing memory subsystems in servers
Connecting DIMMs
via standard DRAM interfaces
directly to the MCs
Using on-DIMM MBs
(FB-DIMMs)
Using on-board MBs
(on the mainboard
or riser cards)
Using low-line-count parallel links
to connect MBs to the MCs
How to connect DIMMs to the MCs?
Connecting DIMMs via low-line-count links and
memory buffers (MBs) to the MCs
Using low-line-count serial links
to connect MBs to the MCs
Using on-board MBs
(on the mainboard
or riser cards)
*

## Slide 113
4. Evolution of Intel’s high-end 2S server processors and platforms
Notes: 113

## Slide 114: 4. Evolution of Intel’s high-end 2S server processors and platforms (1)
4. Evolution of Intel’s high-end 2S server processors and platforms
Based on the design space of implementing memory subsystems in servers
discussed so far and the relevant facts relating to Intel’s high-end platforms,
presented in the next two tables, subsequently, we will give an overview of
how memory systems in Intel’s high-end memory subsytems evolved.

## Slide 115: 4. Evolution of Intel’s high-end 2S server processors and platforms (2)
Platform | Core | Techn. | Date of Intro. | High-end multicore 2S server lines | Core count (up to) | No. and max. speed of memory channels/socket | Kind of connecting memory to the MCH/ Proc. socket
 | Pentium 4 Prescott DP enhanced | 90 nm | 6/2004 | Xeon DP (Nocona) | 1C | 2x DDR2-400 | 2 direct attached DDR2 channels to the MCH PGA 604
 | Pentium 4 Prescott 2M DP enhanced | 90 nm | 10/2005 | Xeon DP 2.8 (Paxville DP) | 2x1C | 2x DDR2-400 | 2 direct attached DDR2 channels to the MCH PGA 604
Bensley | Pentium 4 Presc. | 65 nm | 5/2006 | Xeon 50xx (Dempsey) | 2x1C | 4x DDR2-533 (FB-DIMM) | 4 serial FB-DIMM channels to the MCH LGA 771
 | Core2 | 65 nm | 6/2006 | Xeon 51xx (Woodcrest) | 2C |  | 
 | Core2 | 65 nm | 11/2006 | Xeon 53xx (Clowertown) | 2x2C |  | 
 | Penryn | 45 nm | 11/2007 | Xeon 54xx (Harpertown) | 2x2C |  | 
Kind of memory connections in Intel’s high-end 2S SMP server platforms

## Slide 116: 4. Evolution of Intel’s high-end 2S server processors and platforms (3)
Platform | Core | Techn. | Date of Intro. | High-end multicore 2S server lines | Core count (up to) | No. /max. speed of memory channels/ socket | Kind of connecting memory to the processor/ Proc. socket
Tylersburg | Nehalem | 45 nm | 3/2009 | Xeon 55xx (Nehalem –EP) Gainestown) | 4C | 3x DDR3-1333 | 3 direct attached DDR3 channels LGA 1366
 | Westmere | 32 nm | 3/2010 | Xeon 56xx (Westmere-EP) | 6C |  | 
Boxboro-EX | Nehalem | 45 nm | 3/2010 | Xeon 65xx Nehalem-EX) | 8C | 8x DDR3-1066 | 4 serial (SMI) channels, SMB buffers LGA 1567
 | Westmere | 32 nm | 4/2011 | Xeon E7-28xx (Westmere-EX) | 10C |  | 
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-28xx v2 (Ivy Bridge-EX) | 15C | 8x DDR3-1600 | 4 parallel (SMI2) channels, SMB2 buffers LGA 2011-1
Grantley | Haswell | 22 nm | 9/2014 | E5-26xx v3 (Haswell-EP) | 18C | 4x DDR4-2133 | 4 direct attached DDR4 channels LGA 2011-3
 | Broadwell | 14 nm | 4/2016 | E5-26xx v4 (Broadwell-EP) | 22C |  | 
Purley | Skylake | 14 nm | 7/2017 | Silver 41xx (Skylake-SP) | 28C | 6x DDR4-2400 | 6 direct attached DDR4 channels LGA 3647
 | Cascade Lake | 14 nm | 4/2019 | Silver 42xx Cascade Lake-SP | 28C |  | 
na. | Cascade Lake | 14 nm | 4/2019 | Platinum 92xx Cascade Lake-AP | 2x28 | 12x DDR4- 2933 | 12 direct attached DDR4 channels BGA 5903
Kind of memory connections in Intel’s high-end 2S NUMA server platforms

## Slide 117: 4. Evolution of Intel’s high-end 2S server processors and platforms (4)
Where to connect DIMMs
to the server platform?
Connecting DIMMs
via the MCH
(SMPs)
Connecting DIMMs
directly to the
processors
(NUMAs)
FB-DIMM interface
in Intel's
Bensley (2006/07)
for up to 4 C
Intel's SMI2 interface in
Brickland (2014)
for up to 15C
Intel's SMI interface in
Boxboro EX (2010/11)
for up to 10C
Early 90 nm
Pentium 4
Prescott DP
based platform
for 1C
(2004)
DDR3 interface
in Intel's Tylersburg
(2009) for up to 6C
Connecting DIMMs
via standard DRAM interfaces
directly to the MCs
Using on-DIMM MBs
(FB-DIMMs)
Using on-board MBs
(on mainboard/riser cards)
Using low-line-count parallel links
to connect MBs to the MCs)
How to connect DIMMs to the MCs?
Connecting DIMMs via low-line-count links and
memory buffers (MBs) to the MCs
Overview of connecting memory subsystems in Intel’s 2S server platforms -1
*
DDR4 interface
in Intel's Grantley
(2014/16)
for up to 22C and
Purley (2017/19)
for up to 28C
Using low-line-count serial links
to connect MBs to the MCs
Using on-board MBs
(on mainboard/riser cards)
Standard DRAM
Interface to the MCH in Intel’s
90 nm Pentium 4
Prescott DP (2x1C)
b)
a)
c)
d)
e)

## Slide 118: 4. Evolution of Intel’s high-end 2S server processors and platforms (5)
Overview of connecting memory subsystems in Intel’s 2S server platforms -1
Next, we discuss the individual steps of the outlined evolution of connecting the
memory subsystems to server platforms.

## Slide 119: 4. Evolution of Intel’s high-end 2S server processors and platforms (6)
90 nm Pentium 4
Prescott DP (2x1C)
E7520 MCH
ICH5R/ 6300ESB IOH
FSB
HI 1.5
90 nm Pentium 4
Prescott DP (2x1C)
FSB
DDR-266/333
DDR2-400
65 nm Pentium 4 Prescott DP (2x1C)/ Core2 (2C/2*2C/4C)
Penryn (2C/2x2C)
631*ESB/ 632*ESB IOH
FSB
65 nm Pentium 4 Prescott DP (2x1C)/ Core2 (2C/2*2C/4C)/
Penryn (2C/C)
FBDIMM
w/DDR2-533
First, using low line count serial links and on-DIMM MBs (FB-DIMMs) to
link memory to the MCH (in Pentium 4 Prescott/Core 2-based platforms)
Xeon DP 2.8
/Paxville DP)
Xeon 5000
(Dempsey)
2x1C
Xeon 5100
(Woodcrest)
2C
Xeon 5300
(Clovertown)
2x2C
/
/
ESI
ESI: Enterprise System Interface
4 PCIe lanes, 0.25 GB/s per lane (like the DMI interface,
providing 1 GB/s transfer rate in each direction)
HI 1.5 (Hub Interface 1.5)
8 bit wide, 66 MHz clock, QDR,
66 MB/s peak transfer rate
Xeon 5400
(Harpertown)
2x2C
Xeon 5200
(Harpertown)
2C
/
/
/
1333/1067 MT/s
800 MT/s
90 nm Pentium 4 Prescott DP based
2S platform (2004)
Pentium 4 Prescott DP/Core 2 based
2S platform (2006)
2x240 lines
~4x 50 lines
5000 MCH
(Enhanced)
(Bensley 2S platform)

## Slide 120: 4. Evolution of Intel’s high-end 2S server processors and platforms (7)
A brief introduction to FB-DIMM memories
FB-DIMM memories were standardized and introduced around 2006/2007.
They supported DDR2 memories up to DDR2-667.
MBs are placed onto the DIMMs, as seen in the next Figures, this structure
is called FB-DIMMs.
MBs are connected to the MC or MCs via low line count serial buses.
They perform among others the serial/parallel conversion needed between the
serial MC and parallel DDR interfacess.
*

## Slide 121: 4. Evolution of Intel’s high-end 2S server processors and platforms (8)
Layout of an FB-DIMM based memory subsystem -1 [15]
The standardized FB-DIMM technology implements serial, packet based,
bidirectional, point-to-point links.
It supports a cascaded connection of up to 8 FB-DIMMs.

## Slide 122
4. Evolution of Intel’s high-end 2S server processors and platforms (9)
Layout of an FB-DIMM based memory subsystem -2
The links make use of differential signaling and include 14 read/10 write lanes,
as indicated in the Figure below [2].

## Slide 123: 4. Evolution of Intel’s high-end 2S server processors and platforms (10)
Example:
Block diagram
of Intel’s
Core 2-based
(2x2C)
Xeon 5300
2S server
platform [16]

## Slide 124: 4. Evolution of Intel’s high-end 2S server processors and platforms (11)
1First chipset with PCIe 2.0
ME: Management Engine
Clink: It connects the ME (Management Engine)
to the ICH9/ICH10
b) Moving memory connection from the MCH to the processor and falling back
to direct DRAM connection (in Nehalem-EP/Westmere-EP-based platforms)
ESI: Enterprise System Interface
4 PCIe lanes, 0.25 GB/s per lane (like the DMI interface,
providing 1 GB/s transfer rate in each direction)
55xx IOH1
QPI
QPI
ICH9/ICH10
ESI
QPI
CLink
ME
DDR3-1333
DDR3-1333
Xeon 55xx
(Gainestown)
4C
Xeon 56xx
(Gulftown)
6C
or
Nehalem-EP (4C) Westmere-EP (6C) proc.
Nehalem-EP (4C) Westmere-EP (6C) proc.
E5000 MCH
(Enhanced)
631*ESB/ 632*ESB IOH
FSB
FBDIMM
w/DDR2-533
Xeon 5000
(Dempsey)
2x1C
Xeon 5100
(Woodcrest)
2C
Xeon 5300
(Clovertown)
2x2C
/
/
ESI
Xeon 5400
(Harpertown)
2x2C
Xeon 5200
(Harpertown)
2C
/
/
/
1333/1067 MT/s
65 nm Pentium 4 Prescott DP (2x1C)/ Core2 (2C/2*2C/4C)
65 nm Pentium 4 Prescott DP (2x1C)/ Core2 (2C/2*2C/4C)
SMP based
NUMA based
Pentium 4 Prescott/Core 2 based
2S platform up to 4C (2006)
Nehalem-EP/Westmere-EP based
2S platform up to 6C (2009)
(Tylersburg 2S platform)

## Slide 125: 4. Evolution of Intel’s high-end 2S server processors and platforms (12)
Remark
While introducing DDR3 memories Intel stopped using FB-DIMM memory since
no FB-DIMM memories with DDR3 speed grade became available on the market.
This was caused by the fact that memory vendors cancellled their DDR3-based
FB-DIMM developments due to the low demand for this memory type caused
by its drawbacks (higher dissipation, longer access time and higher price).

## Slide 126: 4. Evolution of Intel’s high-end 2S server processors and platforms (13)
Montecito (2C) (2006)
Opteron server lines (1C) (2003)
Opteron server lines (2C) 2005)
and all subsequent AMD lines
PA-8800 (2004)
PA-8900 (2005)
and all previous PA lines
Core 2 Duo line (2C) (2006)
and all preceding Intel lines
Core 2 Quad line (2x2C) (2006/2007)
Penryn line (2x2C) (2008)
Nehalem lines (4) (2008)
and all subsequent Intel lines
Tukwila (4C) (2010)
AMD’s K7 lines (1C)
(1999-2003)
UltraSPARC III (1C) (2001)
and all subsequent Sun lines
UltraSPARC II (1C) (~1997)
Connection point of memory
Connecting memory to the processor(s)
(NUMA)
Connecting memory to the MCH
(SMP)
Transition of the memory connection in the evolution of processors
POWER1 (RS/6000) (1990)
direct connection via external circuitry
since POWER5 (2C) (2005)
on-die integrated mem. controller

## Slide 127: 4. Evolution of Intel’s high-end 2S server processors and platforms (14)
Nehalem-EX (8C) Westmere-EX (10C)
QPI
QPI
ICH10
ESI
7500 IOH
QPI
Nehalem –EP (4C)
Westmere-EP (6C)
34xx PCH
ESI
QPI
DDR3-1333
DDR3-1333
ME
Xeon 5500
(Gainestown)
Xeon 5600
(Gulftown)
or
Nehalem-EX (8C) Westmere-EX (10C)
or
Xeon 6500
(Nehalem-EX)
(Becton)
Xeon E7-2800
(Westmere-EX)
ME
c) Connecting DDR3 DIMMs via low line count serial links and on-board MBs
to raise nc (in Nehalem-EX/Westmere-EX-based platforms)
Nehalem –EP (4C)
Westmere-EP (6C)
DDR3-1067
SMB
SMB
SMB
SMB
SMB
SMB
DDR3-1067
SMB
SMB
QPI
Nehalem-EP/Westmere-EP based 2S platform (2009)
Nehalem-EX/Westmere-EX based 2S platform (2010)
SMI
SMI
The SMI link is very similar to the
FB-DIMM interface, it is a serial, packet based, differential link including 54 signal lines.
(Tylersburg 2S platform)
(Boxboro 2S platform)
nc: Number of memory channels

## Slide 128: 4. Evolution of Intel’s high-end 2S server processors and platforms (15)
Remarks to the SMI interface and the Scalable Memory Buffer (SMB) [17]
The southbound (SB) input link is 10 lanes wide (plus an 11th spare lane) and
carries commands and write data from the host memory controller.
The northbound output link is 13 lanes wide (plus a 14th spare lane) and
carries read return data or status information from the Intel 7500/7510/7512
Scalable Memory Buffer back towards the host.
Intel’s SMI interface has very few protocol changes to the FB-DIMM interface.
It is a bidirectional link interface using high-speed differential point-to-point
electrical signaling.
Figure: The Scalable Memory Buffer (SMB) and Scalable Memory Interface (SMI) [17]

## Slide 129: 4. Evolution of Intel’s high-end 2S server processors and platforms (16)
In addition, Intel 7500/7510/7512 Scalable Memory Buffer has a differential
forwarded clock lane in each direction.
Intel’s 7500/7510/7512 Scalable Memory Buffer supports SMI interface speeds
of 4.8 Gbps, 5.86 Gbps and 6.4 Gbps
Remarks to the SMI interface and the Scalable Memory Buffer (SMB) -2 [17]

## Slide 130: 4. Evolution of Intel’s high-end 2S server processors and platforms (17)
On-board SMB
PCH
Example: Connecting DDR3 DIMMs via low line count serial links and on-board
MBs to the processors (in Westmere-EX-based platforms) [14]

## Slide 131: 4. Evolution of Intel’s high-end 2S server processors and platforms (18)
QPI
QPI
Up to DDR3-1067 for Xeon 6500/7500
Up to DDR3-1333 for Xeon E7-2800
SMB
SMB
SMB
SMB
ICH10
ESI
SMB
SMB
SMB
SMB
7500 IOH
QPI
/
Xeon 6500/7500
(Nehalem-EX)
(Becton)
Xeon E7-2800
(Westmere-EX) 2S
Nehalem-EX (8C) Westmere-EX (10C)
Nehalem-EX (8C) Westmere-EX (10C)
QPI 1.1
DMI2
Up to DDR3-1600
SMB
SMB
SMB
SMB
Up to DDR3-1600
SMB
SMB
SMB
SMB
C602 PCH
DMI2
/
Xeon E7-2800 v2
(Ivy Bridge-EX 2S)
Xeon E7-2800 v2
(Ivy Bridge-EX 2S
Ivy Bridge -EX (15C)
Ivy Bridge -EX (15C)
QPI 1.1
Nehalem-EX/Westmere-EX based 2S platform for up to 10C (2010)
Ivy Bridge based 2S platform for up to 15C (2014)
Up to DDR3-1067 for Xeon 6500/7500
Up to DDR3-1333 for Xeon E7-2800
SMI
SMI
SMI2
SMI2
d) Introducing low line count parallel links to reduce dissipation by removing
serial-parallel conversion in Ivy Bridge-EX-based 2S platforms
(Boxboro 2S platform)
(Brickland 2S platform)

## Slide 132: 4. Evolution of Intel’s high-end 2S server processors and platforms (19)
The SMI link of the Boxboro-EX platform was a serial, packet based, bidirectional
differential link including 54 signal lines.
By contrast, with the SMI2 link Intel changed to 64-bit parallel, bidirectional
communication using single-ended voltage reference signals, called VMSE
(Voltage Mode Single Ended) signaling.
SMI 2 requires altogether about 110 signal lines, i.e. about 100 % more lines
than SMI.
Presumable, Intel changed from serial transfer to parallel transfer to avoid
serial/parallel conversion and thus to reduce dissipation.
Low line count parallel links

## Slide 133: 4. Evolution of Intel’s high-end 2S server processors and platforms (20)
LVDS: Low Voltage Differential Signaling LVTTL: Low Voltage TTL
(D)RSL: (Differential) Rambus Signaling Level SSTL: Stub Series Terminated Logic VCM: Common Mode Voltage VREF: Reference Voltage
VMSE: Voltage Mode Single Ended FB-DIMM: Fully Buffered DIMM
LVTTL (3.3 V)
FPM/EDO
SDRAM
HI 1.5
TTL (5 V)
FPM/EDO
SSTL
SSTL2 (DDR)
SSTL1.8 (DDR2)
SSTL1.5 (DDR3)
SSTL1.2 (DDR4)
RSL (RDRAM)
FSB
VMSE (SMI2)
LVDS
PCIe
QPI, DMI, ESI
FB-DIMMs
DRSL
XDR (data)
IMI, SMI
Signaling systems used in buses
Signals
Single ended
voltage referenced
Single ended
ground referenced
Differential
t
t
VREF
t
S+
S-
VCM
Typ.voltage
swings
600-800 mV
200-300 mV
3.3-5 V
Signaling
system
used in
*

## Slide 134: 4. Evolution of Intel’s high-end 2S server processors and platforms (21)
e) Falling back to direct connecting DIMMs to the processors in order to
reducing dissipation in Haswell-EP/Broadwell-EP-based 2S platforms
QPI 1.1
DMI2
Up to DDR4-2133
Up to DDR4-2133
C612 PCH
DMI2
/
Xeon E5-2600 v3/v4
(Haswell-EP/
Broadwell-EP 2S)
Xeon E5-2600 v3/v4
(Haswell-EP/
Broadwell-EP 2S
Haswell-EP (18C)
Broadwell-EP (22C)
Haswell-EP (18C)
Broadwell-EP (22C)
QPI 1.1
Haswell-EP/Broadwell-EP based 2S platform for up to 22C (2014)
QPI 1.1
DMI2
Up to DDR3-1600
Up to DDR3-1600
C602 PCH
DMI2
/
Xeon E7-2800 v2 2S)
Xeon E7-2800 v2 2S
Ivy Bridge -EX (15C)
Ivy Bridge -EX (15C)
QPI 1.1
Ivy Bridge based 2S platform for up to 15C (2014)
SMI2
SMI2
(Grantley 2S platform)
(Brickland 2S platform)
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB

## Slide 135: 4. Evolution of Intel’s high-end 2S server processors and platforms (22)
Example: Haswell-EP/
Broadwell-EP-based
platform [18]

## Slide 136: 4. Evolution of Intel’s high-end 2S server processors and platforms (23)
Example: Haswell-EP/
Broadwell-EP-based
motherboard [18]

## Slide 137: 4. Evolution of Intel’s high-end 2S server processors and platforms (24)
Skylake-SP/Cascade Lake-SP based 2S platform for up to 28C (2017)
UPI
DMI3
Up to DDR4-2400
Up to DDR4-2400
C621/C622 PCH
DMI3
/
Xeon Silver 41xx/42xx
(Skylake-SP/
Cascade Lake-SP 2S)
Xeon Silver 41xx/42xx
(Skylake-SP/
Cascade Lake-SP 2S)
UPI
Skylake-SP (28C)
Cascade Lake-SP (28C)
Skylake-SP (28C)
Cascade Lake-SP (28C)
UPI: 10.4 GT/s
QPI 1.1
DMI2
Up to DDR4-2133
Up to DDR4-2133
C612 PCH
DMI2
/
Xeon E5-2600 v3/v4
(Haswell-EP/
Broadwell-EP 2S)
Xeon E5-2600 v3/v4
(Haswell-EP/
Broadwell-EP 2S
Haswell-EP (18C)
Broadwell-EP (22C)
Haswell-EP (18C)
Broadwell-EP (22C)
QPI 1.1
Haswell-EP/Broadwell-EP based 2S platform for up to 22C (2014)
DMI3: 8GB/s
Increasing the number of per processor memory channels from 4 to 6
in the Skylake-SP/Cascade Lake-SP-based platforms
DMI2: 4 GB/s
(Grantley
platform)
(Purley
platform)

## Slide 138: 4. Evolution of Intel’s high-end 2S server processors and platforms (25)
Example: Skylake-SP/
Cascade Lake-SP-based platform [19]
C621/C622

## Slide 139: 4. Evolution of Intel’s high-end 2S server processors and platforms (26)
Example: Skylake-SP/
Cascade Lake-SP-based motherboard [19]
Up to DDR4-2933

## Slide 140: 4. Evolution of Intel’s high-end 2S server processors and platforms (27)
Platform | Core | Techn. | Date of Intro. | High-end multicore 2S server lines | Core count (up to) | No./speed of mem. channels per socket (up to) | Scaled nM per socket | Per core BW rel. to ref. platform
Reference platform | Pentium 4 Prescott DP | 90 nm | 6/2004 | 90 nm Nocona | 1C | 1x DDR2/400 | 1.0 | 1.0
 | Pentium 4 Presc. | 90 nm | 10/2005 | Xeon DP 2.8 (Paxville DP) | 2x1C | 1x DDR2/400 | 1.4 | 0.5
Bensley | Pentium 4 Presc. | 65 nm | 5/2006 | Xeon 5000 (Dempsey) | 2x1C | 2x DDR2/667 | 1.4 | 1.7
 | Core2 | 65 nm | 6/2006 | Xeon 5100 (Woodcrest) | 2C | 2x DDR2/667 | 1.4 | 1.7
 | Core2 | 65 nm | 11/2006 | Xeon 5300 (Clowertown) | 2x2C | 2x DDR2/667 | 2.0 | 0.8
 | Penryn | 45 nm | 11/2007 | Xeon 5400 (Harpertown) | 2x2C | 2x DDR2/667 | 2.0 | 0.8
Tylersburg | Nehalem | 45 nm | 3/2009 | Xeon 55xx (Gainestown) | 4C | 3x DDR3/1333 | 2.0 | 2.5
Boxboro-EX | Nehalem | 45 nm | 3/2010 | Xeon X6500 Nehalem-EX) | 8C | 8x DDR3/1066 | 2.8 | 2.7
 | Westmere | 32 nm | 4/2011 | Xeon E7-28xx (Westmere-EX) | 10C | 8x DDR3/1333 | 3.2 | 2.7
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-28xx v2 (Ivy Bridge-EX) | 15C | 8x DDR3/1600 | 3.9 | 2.1
Grantley | Haswell | 22 nm | 9/2014 | E5-2600xx v3 (Haswell-EP) | 18C | 4x DDR4/2133 | 4.2 | 1.2
 | Broadwell | 14 nm | 4/2016 | E5-26xx v4 (Broadwell-EP) | 22C | 4x DDR4/2400 | 4.7 | 1.1
Purley | Skylake | 14 nm | 7/2017 | Silver 41xx Skylake-SP) | 28C | 6x DDR4/2400 | 5.3 | 1.3
 | Cascade Lake | 14 nm | 4/2019 | Silver 41xx Skylake-SP) | 28C | 6x DDR4/2933 | 5.3 | 1.6
Relative per core bandwidth in Intel’s 2S server platforms (recap) -1

## Slide 141: 4. Evolution of Intel’s high-end 2S server processors and platforms (27)
Relative per core bandwidth in Intel’s 2S server platforms (recap) -2
Let’s take Intel’s early single-core Nocona-based platform as a reference platform
for considering the per core memory bandwidth provided by the enlisted
high-end 2S platforms.
Data in the last but one column shows the number of memory channels needed
for the same per-core memory bandwidth as provided by the reference platform
whereas the last column (Per core BW rel. to ref. platform) provides a comparison
about the actual bandwidth of the discussed platform relative to the reference
platform.
It can be stated that over generation the relative memory bandwidth remained
about the same mainly with the exception of the platforms with low line count
serial and parallel interfaces (Nehalem/Westmere-based server platforms).
In these platforms Intel provided 2.5 – 2.7 times higher bandwidth than the
reference platform but corrected it in their subsequent direct attached designs
(beginning with the Haswell-based platform).
*

## Slide 142
5. AMD’s EPYC server processors and platforms
5.1 The 1. gen. Naples EPYC server line
5.2 The 2. gen. Rome EPYC server line
Section 5. will not be discussed.
Notes: 142

## Slide 143: 5. AMD’s EPYC server processors and platforms (1)
9. The EPYC server lines
AMD unveiled until now two generations of EPYC processor lines:
the 1. generation, called Naples line, launched in 06/2017 and
the 2. generation, called Rome line, introduced in 11/2018, launched in 08/2019.
These two generations will be discussed subsequently.

## Slide 144
5.1 The 1. gen. Naples EPYC server line
Notes: 144

## Slide 145: 5.1 The 1. gen. Naples EPYC server line (1)
AMD's Zen-based processor lines
ThreadRipper
(HED)
Ryzen Mobile
(mobil)
Ryzen
(DT)
EPYC
(1S/2S server)
5.1 The 1. gen. Naples EPYC server line -1
Positioning AMD's 1. gen. EPYC server line in AMD’s 1.gen. Zen-based lines
Single CCX +
Vega GPU
Zeppelin chip
(2x CCX, no GPU)
2 Zeppelin chips
interconnected by the IF,
implemented as an MCM
4 Zeppelin chips
interconnected by the IF,
implemented as an MCM
Drawings based on [20]

## Slide 146: 5.1 The 1. gen. Naples EPYC server line (2)
Launched in 6/2017 based on the Zen core, manufactured on 14 nm technology.
It covers 1S and 2S servers.
Figure : Recent market share of 1S and 2S servers [2]
The 1. gen. Naples EPYC server line -2
The reason why AMD focuses on up to 2S servers is that these servers cover
recently over 90 % of the server market, as indicated below.

## Slide 147: 5.1 The 1. gen. Naples EPYC server line (3)
The EPIC package [21]
Package size: 58 x 75 mm, LGA 4094 socket (SP3).

## Slide 148: 5.1 The 1. gen. Naples EPYC server line (4)
Main features of AMD's EPYC line introduced in 2017
AMD's Zen-based processor lines introduced in 2017
 | Ryzen Mobile APU (Raven Ridge) | Ryzen DT (Summit Ridge) | ThreadRipper (Whitehaven) | EPYC (Naples)
Market segment | Mobile | Desktop platform | HED | 1S/2S server
μarch./Technology | Zen 14 nm | Zen, 14 nm | Zen, 14 nm | Zen, 14 nm
Launched models | Ryzen 7 2700U Ryzen 5 2500U (10/2017) | Ryzen 7 (3/2017) Ryzen 5 (4/2017) Ryzen 3 (7/2017) | 1950X/1920X/1900X (8/2017) | Series 7xx1 (6/2017)
Layout | CCX + Vega 8/10 | Zeppelin die with 2x CCX | MCM (2x Zeppelin die) | MCM (4x Zeppelin die)
Integrated GPU | Yes | No | No | No
Core count | 4 | 4/6/8 | 8/12/16 | 8/16/24/32
SMT | SMT | SMT (except Ryzen 3) | SMT | SMT
Mem. channels/rate | 2xDDR4-2400 | 2xDDR4-2666 | 4xDDR4-2666 | 8xDDR4-2666
PCIe 3.0 lanes | ?? | 16xPCIe 3.0 | 60xPCIe 3.0 | 128 for 1S servers 64 for 2S servers
TDP | 15 W | 65/95 W | 180 W | 120/170/180 W
Socket | AM4 (1331) | AM4 (1331) | TR4 (SP3r2) (4094) | SP3 (4094)
Chipset | SoC | 300-series | X399 | No chipset, SOC

## Slide 149: 5.1 The 1. gen. Naples EPYC server line (5)
Die-to-die interconnections in a 1S EPYC server processor
A 1S EPYC server processor is built up of 4 Zeppelin dies interconnected by a crossbar
Infinity Fabric switch and implemented as an MCM (Multi-chip_Module), as shown
in the Figure below.
Figure: Die interconnections in an 1S EPYC server [21]
32-bit per link per direction
interconnecting the chips
in a crossbar fashion
by single-ended signals
with a bandwidth of 42.8 GB/s
per link in each direction.

## Slide 150: 5.1 The 1. gen. Naples EPYC server line (6)
MA-MH: 8 x 72-bit DDR4
DRAM channels
Up to 2 TB DDR4 memory
∞: Die-to-die IF links
16-bit per link per direction
interconnecting the chips
in a crossbar fashion
by single-ended signals
(2 pJ/bit TDP)
with a bandwidth of 42.6 GB/s
per link in each direction.
A more detailed presentation of a 1S EPYC server processor [22]
G0 - G3: 4 x 16 SERDES lanes
(in each direction)
Used for socket-to-socket
communication
P0 - P3: 4 x 16 SERDES lanes
(in each direction)
Used to implement PCIe 3.0 lanes

## Slide 151: 5.1 The 1. gen. Naples EPYC server line (7)
Dies and die interconnections within a 1S EPYC server [23]
A: 4 Zeppelin dies/socket B: A single Zeppelin die

## Slide 152: 5.1 The 1. gen. Naples EPYC server line (8)
MCM-to-MCM interconnections in a 2S EPYC server processor
A 2S EPYC server processor is built up 2 EPYC processors that are interconnected
by the Infinity Fabric (IF), as shown in the Figure.
Figure: Built up of a 2S EPYC server [21]
Up to 2x 32 cores,
2x 4 channel DDR4 memory,
up to 2x 2 TB memory,
2x 64 PCIe 3 lanes
4x die-to-die IF links
16 differential lanes per direction
(9 pJ/bit TDP)
interconnecting related dies
on the two sockets,
37.9 GB/s bandwidth bidirectional.
(Up to two hops are needed
for die-to-die transfers).

## Slide 153: 5.1 The 1. gen. Naples EPYC server line (8b)
Layout of a dual socket EPYC system [24]

## Slide 154: 5.1 The 1. gen. Naples EPYC server line (9)
GMI: Global Memory Interconnect
SDF: Scalable Data Fabric
4x 16 lanes per direction
37.9 GB/s
bidir.
37.9 GB/s
bidir.
37.9 GB/s
bidir.
37.9 GB/s
bidir.
42.6 GB/s bidir.
42.6 GB/s bidir.
MCM-to MCM IF interconnections in a 2S EPYC server processor - detailed [25]

## Slide 155: 5.1 The 1. gen. Naples EPYC server line (10)
Comparing memory latencies in Intel’s Xeon and AMD’s EPYC [26]

## Slide 156: 5.1 The 1. gen. Naples EPYC server line (11)
An Epic processor has 8 x 16 serialization-deserialization circuits (called SERDES)
that can be used either for implementing the interconnection lanes between
two sockets of a 2S server processor or PCIe 3.0 lanes, as indicated below.
G0 - G3: 4 x 16 SERDES circuits
(in each direction)
Used for PCIe 3.0 lanes in 1S
and for MCM-to-MCM
interconnection lanes
in a 2S configuration
P0 - P3: 4 x 16 SERDES lanes
(in each direction)
Used for PCIe 3.0 lanes
Figure: High-level block diagram of a Ryzen processor
Restrictions on the number of PCIe 3.0 lanes per socket -1

## Slide 157: 5.1 The 1. gen. Naples EPYC server line (12)
In a 1S EPYC processor all SERDES circuits are available for PCIe 3.0 lanes,
thus 1S EPYC server processors can provide 6x16 = 128 PCIe 3.0 lanes.
By contrast, in 2S EPYC processors 4x16 lanes are needed to interconnect both
sockets, then only 4x 16 = 64 PCIe 3.0 lanes can be implemented per socket.
This design approach implies however, a serious restriction on the feasible
server configurations since a 4S configuration would require already 2x 64 lanes,
i.e. all 128 available SERDES circuits for interconnecting 4 sockets, consequently,
for a 4S configuration no PCIe 3 lanes could be provided.
In other words, the chosen IF solution allows only to implement 1S or 2S
configurations.
AMD is full aware of this restriction and did not announce any plans to develop
4S or 8S servers while employing IF.
This is understandable due to the low market share of 4S and 8S servers
vs. 1S and 2S servers.
Restrictions on the number of PCIe 3.0 lanes per socket -2

## Slide 158: 5.1 The 1. gen. Naples EPYC server line (13)
Width and bit rate of Infinity Fabric links in an EPYC processor [27]
Remarks
1) From the 4 available Cross-Sectional Links per die only 3 are needed
to interconnect the actual die with the further three dies of the processor.
2) The Die-to-Die interconnects are actually not differential lanes but single-ended
lines to reduce power consumption (resulting in 2 pJ/bit vs. 9 pJ/bit TDP.

## Slide 159: 5.1 The 1. gen. Naples EPYC server line (14)
Additional features of EPYC-7000-series processors
a) Workload aware power management
b) Per core frequency and voltage scaling
c) Integrated secure processor

## Slide 160: 5.1 The 1. gen. Naples EPYC server line (15)
a) Workload aware power management of the EPYC line [21]

## Slide 161: 5.1 The 1. gen. Naples EPYC server line (16)
b) Per-core frequency and voltage scaling [21]
LDO: Low Drop Out Voltage Regulator

## Slide 162: 5.1 The 1. gen. Naples EPYC server line (17)
c) Integrated secure processor [28]

## Slide 163: 5.1 The 1. gen. Naples EPYC server line (18)
 | Cores Threads | Frequency (GHz) |  |  | L3 | DRAM | PCIe | TDP | Price
 |  | Base | All | Max |  |  |  |  | 
EPYC 7551P | 32 / 64 | 2.0 | 2.6 | 3.0 | 64 MB | 8 Ch DDR4 up to 2666 MT/s | 8 x16 PCIe | 180W | $2100
EPYC 7401P | 24 / 48 | 2.0 | 2.8 | 3.0 |  |  |  | 155W/170W | $1075
EPYC 7351P | 16 / 32 | 2.4 | 2.9 |  |  |  |  | 155W/170W | $750
Main features of AMD's 1S EPYC-7000 series processors [21]
Note that the P tag means 1S configuration.
The last numeric character in the model designation, i.e. 1 indicates generation 1.

## Slide 164: 5.1 The 1. gen. Naples EPYC server line (19)
 | Cores Threads | Frequency (GHz) |  |  | L3 | DRAM | PCIe | TDP | Price
 |  | Base | All | Max |  |  |  |  | 
EPYC 7601 | 32 / 64 | 2.20 | 2.70 | 3.2 | 64 MB | 8 Ch DDR4 up to 2666 MT/s | 8 x16 PCIe | 180W | $4200
EPYC 7551 | 32 / 64 | 2.00 | 2.55 | 3.0 |  |  |  | 180W | >$3400
EPYC 7501 | 32 / 64 | 2.00 | 2.60 | 3.0 |  |  |  | 155W/170W | $3400
EPYC 7451 | 24 / 48 | 2.30 | 2.90 | 3.2 |  |  |  | 180W | >$2400
EPYC 7401 | 24 / 48 | 2.00 | 2.80 | 3.0 |  |  |  | 155W/170W | $1850
EPYC 7351 | 16 / 32 | 2.40 | 2.9 |  |  |  |  | 155W/170W | >$1100
EPYC 7301 | 16 / 32 | 2.20 | 2.7 |  |  |  |  | 155W/170W | >$800
EPYC 7281 | 16 / 32 | 2.10 | 2.7 |  | 32 MB |  |  | 155W/170W | $650
EPYC 7251 | 8 / 16 | 2.10 | 2.9 |  |  |  |  | 120W | $475
Main features of AMD's 2S EPYC-7000 series processors [21]

## Slide 165: 5.1 The 1. gen. Naples EPYC server line (20)
Layout of a 2S EPYC server [2]
Note that it does not require a PCH.

## Slide 166: 5.1 The 1. gen. Naples EPYC server line (21)
Example EPYC 2S motherboard (SuperMicro's H11DSi) -1 [29]
1. Dual AMD EPYC™ 7000-Series
Processors
2. 2TB Registered ECC DDR4 2666MHz SDRAM in 16 DIMMs
3. Expansion slots: 2 PCI-E 3.0 x16 3 PCI-E 3.0 x8
4. 10 SATA3, 1 M.2, 2 SATA DOM
5. Dual Gigabit Ethernet LAN Ports
6. ASPEED AST2500 BMC graphics
7. Up to 2 USB 3.0 ports Up to 4 USB 2.0 ports
8. 8 4-pin PWM Fan & Speed control

## Slide 167: 5.1 The 1. gen. Naples EPYC server line (22)
Example block diagram of a 2S EPYC server platform [30]

## Slide 168: 5.1 The 1. gen. Naples EPYC server line (23)
Performance comparison AMD's EPIC vs. Intel's Broadwell server line
models while running the SPECint_rate_base2006 benchmark [21]

## Slide 169
5.2 The 2. gen. Rome EPYC server line
Notes: 169

## Slide 170: 5.2 The 2. gen. Rome EPYC server line (1)
Introduced in 11/2018, sampled in Q4 2018, launched in 08/2019.
It is based on the Zen 2 core and is fabricated on 7 nm technology (TSMC).
It covers 1S and 2S servers.
5.2 The 2. gen. EPYC Rome server line -1

## Slide 171: 5.2 The 2. gen. Rome EPYC server line (1b)
AMD's Zen/Zen+ based processor lines introduced in 2019
The 2. gen. Rome EPYC server line -2
 | 2.G Ryzen Mobil APU (Picasso) | 3. G Ryzen DT (Matisse) | 2. G EPYC (Rome) | 
μarch./tech. | Zen+/12 nm | Zen 2/7 nm | Zen2/7 mm | 
Launched models | Ryzen 7 3750H/3700U Ryzen 5 3550H/3500H Ryzen 3 3300U/3200U (1/2019) | Ryzen 9 3950X/3900X Ryzen 7 3800X/3700X Ryzen 5 3600X (7/2019) | EPYC 7xx2 (2P server) EPYC 7xx2P (1P server) (8/2019) | 
Layout | CCX + Vega 10/8/3 | 2xCCD + cIOD | 8 dies, each one 2xCCX+ IO die | 
Integrated GPU | Yes | No | No | 
Core count | 2/4 | Up to 16C | Up to 64C | 
SMT (Multithreaded) | Yes | Yes | Yes | 
Mem. channels/ data rate | 2xDDR4-2400 | 2xDDR4-3200 | 8xDDR4-3200 | 
PCIe lanes | ?? | 16+4+4 | 128 Gen4 | 
TDP | H:35W U:15 W | 65/95/105 W | 120-250 W | 
Socket | FP5 | FP4 | SP3 (4094) | 
Chipset | SoC | SoC | SoC | 

## Slide 172: 5.2 The 2. gen. Rome EPYC server line (2)
AMD’s x86 CPU market share [31]

## Slide 173: 5.2 The 2. gen. Rome EPYC server line (3)
Performance benefits of AMD’s 2. G RYZEN (Rome) [32]

## Slide 174: 5.2 The 2. gen. Rome EPYC server line (4)
Layout of the 2. gen. Rome EPYC server line -1
Novel layout based on an I/O die (manufactured on 14 nm) and 8 core chiplet,
each with 8 Zen 2 cores, manufactured on 7 nm, as indicated below.
Figure: Layout of the 1. gen. Naples and 2. gen. Rome EPYC processors [33]

## Slide 175: 5.2 The 2. gen. Rome EPYC server line (5)
More detailed layout of the 2. gen. EPYC server processor (Rome) [32]

## Slide 176: 5.2 The 2. gen. Rome EPYC server line (6)
Layout of EPYC processors contrasted with the monolithic design [32]

## Slide 177: 5.2 The 2. gen. Rome EPYC server line (7)
Key features of 2. gen. EPYC server processors (Rome) [32]

## Slide 178: 5.2 The 2. gen. Rome EPYC server line (8)
Further features of the 2. gen. EPYC (Rome) server processors
Greatly improved Infinity Fabric speed.
Ability to connect GPUs via the I/O chip and Infinity Fabric protocol without using
PCIe lanes.
Socket compatibility with 1. gen. EPYC (Naples) processors.

## Slide 179: 5.2 The 2. gen. Rome EPYC server line (9)
Mem Hierarchy |  | AMD EPYC 7742 DDR4-3200 | AMD EPYC 7601 DDR4-2400 | Intel Xeon S DDR4-2666 | Intel Xeon E5-2699v4 DDR4-2400
L1 Cache cycles |  | 4 cycles | 4 cycles | 4 cycles | 4 cycles
L2 Cache cycles |  | 12 cycles | 12 cycles | 14-22 cycles | 12-15 cycles
L3 Cache | 2 MB | 14 ns | 14 ns | 22 ns | 21 ns
 | 4 MB | 14 ns | 15 ns | 24 ns | 21 ns
 | 8 MB | 22 ns | 44 ns | 29 ns | 21 ns
16-32 MB |  | 73-132 ns | 88-92 ns | 29-37 ns | 33-79 ns
DRAM 384-512 MB |  | 158-163 (nps = 4) 161-168 ns (worst) | 96-98 ns | 89-91 ns | 95 ns
Cache and memory latencies [34]

## Slide 180: 5.2 The 2. gen. Rome EPYC server line (10)
The IO subsystem of 2. gen. EPYC (Rome) server processors [32]

## Slide 181: 5.2 The 2. gen. Rome EPYC server line (11)
Picture of the 2. gen. Rome EPYC server (11/2018) -2
AMD has already started sampling EPYC 'Rome' processors in about Q3/2018.

## Slide 182: 5.2 The 2. gen. Rome EPYC server line (12)
2-socket 2. gen. EPYC Rome server configuration with 3 IF 2.0 links [32]

## Slide 183: 5.2 The 2. gen. Rome EPYC server line (13)
Main features of dual-socket 2. gen. EPYC (Rome) server processors [35]

## Slide 184: 5.2 The 2. gen. Rome EPYC server line (14)
Main features of single-socket 2. gen. EPYC (Rome) server processors [35]

## Slide 185: 5.2 The 2. gen. Rome EPYC server line (15)
Intel’s response to AMD’s Rome, announced in 08/2018 at Hot Chips 30 [36]
Note that it is implemented as a Multi-Chip_Package with 48 cores, to be launched
in H1 2019 on advanced 14 nm technology.

## Slide 186: 5.2 The 2. gen. Rome EPYC server line (16)
Performance comparison of various recent server processors
(Geometric mean of all test runs [37]

## Slide 187
6. Platform issues of server platforms
6.2 Inter-processor interconnects in server platforms
6.1 Intra-processor interconnects in server processors
6.3 Connection of PCIe lanes to 2S server platforms
Notes: 187

## Slide 188
6.1 Intra-processor interconnects in servers
Notes: 188

## Slide 189: 6.1 Intra-processor interconnects in server processors (1)
6.1 Intra-processor interconnects in server processors
Intra-processor interconnects
in server processors
Interconnects in server platforms
Inter-processor interconnects
in server platforms

## Slide 190: 6.1 Intra-processor interconnects in server processors (2)
CPU
IO C.
GPU
Disp
C.
MC
C: Controller
Intra-processor interconnects in server processors -1
Their aim is to interconnect the functional units of server processors, as indicated
in the Figure below.
Figure: Funcional units of a processor that need to be linked together
by an intra-processor interconnect

## Slide 191: 6.1 Intra-processor interconnects in server processors (3)
Key aspects for implementing intra-processor interconnects
Whether the processors
include individual CPU cores
or core clusters?
Key aspects of implementing intra-processor interconnects
Whether the processors are implemented as monolithic dies or MCMs?
Section a)
Section b)

## Slide 192: 6.1 Intra-processor interconnects in server processors (4)
L3 slice
CPU
core
L1
L2
CPU
core
L1
L2
CPU
core
L1
L2
CPU
core
L1
L2
*
CPU
core
L1/L2
CPU building blocks of multicore server processors
Individual cores based
implementations
Core cluster implementations
Dual-core
core clusters
Quad-core
core clusters
CPU
core
L1
CPU
core
L1
L3 slice
Shared L2
AMD’s Opteron-based
Compute Module
(with shared FP unit)
(2011-2012)
AMD’s Zen-based
CCX (Core CompleX)
(2017-)
Intel’s multicore
servers
(2005-)
L3 slice
Examples
IBM POWER 9 (2017)
a) Whether the processors include individual CPU cores or core clusters?
It is the task of the intra-processor interconnect to link together either individual cores
or core clusters with further building blocks of the processor.
CPU cores may be implemented either as individual cores or core clusters, as shown
below.

## Slide 193: 6.1 Intra-processor interconnects in server processors (5)
Monolithic implementation
Multi-Chip-Module (MCM) implementation
Design paradigms for segmenting multicore processors
All cores are implemented
on the same die
Cores are implemented on a number of dies,
they are properly interconnected and
mounted into the same package
b) Whether the processors are implemented as monolithic dies or MCMs?
Intel's Skylake-SP (2017) [38]
AMD's EPYC (2017) [38], [27]
Up to 28 cores
Up to 4x8 cores
Single package
Example
*

## Slide 194: 6.1 Intra-processor interconnects in server processors (6)
Monolithic implementation
Multi-Chip-Module (MCM) implementation
Design paradigms for segmenting multicore processors
The kind of interconnects needed for monolithic and MCM iprocessor
implementing an on-die or off-die interconnect?
Clearly, monolitic processor implementations make use of on-die interconnects and
MCM implementations off-die interconnects (or in a wider sense on-package
integration), as indicated below.
On-die interconnects
In addition: Off-die interconnects between chips
(On-package integration)

## Slide 195: 6.1 Intra-processor interconnects in server processors (7)
Intra-processor interconnects in server processors -2
Subsequently, we are concerned only with monolithic processor implementations,
i.e. we discuss only on-die interconnects.
On package integration of multiple dies are dealt with in another chapter
(entitled as On-pakage integration).
Nevertheless, the same kind of interconnects can be employed whether individual
CPU cores or core clusters are used.

## Slide 196: 6.1 Intra-processor interconnects in server processors (8)
Crossbar
MC
IO
--
C
--
C
Ring bus
MC
IO
--
C
C
C
--
--
R
R
R
R
R
C
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
C
C
C
C
C
C
C
C
C
MC
C
C
C
MC
C
C
C
C
C
MC
MC
R
R
R
R
R
IO
IO
MC
MC
IO
IO
P
C
R: Router
MC: Memory Controller
Crossbar-based
interconnects
Ring bus-based
interconnect topology
2D mesh-based
interconnect
On-die interconnects in high end server processors
C: Individual CPU core or core cluster
On-die interconnects used in recent server processors
There are three major types of on-die interconnects used in recent server processors,
as seen in the Figure below.

## Slide 197: 6.1 Intra-processor interconnects in server processors (9)
The need for cache coherent on-die interconnects
Obviously, the entire server system needs to be cache coherent, thus all three
alternatives of the indicated on-die interconnects should be cache coherent.
This is a rather sophisticated issue that we do not discuss in this lecture note,
but give a glimpse of its implementation related to Intel’s on-die data ring
(see next Figure).

## Slide 198: 6.1 Intra-processor interconnects in server processors (10)
Implementing cache coherency in Intel’s on-die data ring [39]

## Slide 199: 6.1 Intra-processor interconnects in server processors (11)
a) Crossbar based on-die interconnects in server processors
Crossbar-based on-die interconnects were widely used in Intel’s and AMD’s
multicore servers in the beginning of the 2010’s and off-die interconnects are
also employed in AMD’s recent EPYC server lines to interconnect multiple dies,
as indicated in the next Figures.

## Slide 200: 6.1 Intra-processor interconnects in server processors (12)
Example 1: Five-way crossbar switch as part of Intel’s QPI-based cache-
coherent interconnect in Nehalem based Xeon 5500 processors (2010)
(Crossbar)

## Slide 201: 6.1 Intra-processor interconnects in server processors (13)
Example 2: Crossbar switch in AMD’s Orochi die underlying their 2S and
4S (2 dies) Buldozer-based server processors (2011) []
It incorporates 4 Bulldozer-modules (8 cores) []

## Slide 202: 6.1 Intra-processor interconnects in server processors (14)
Example 3: Off-die crossbar switch in AMD’s Zen-based EPYC server
processors that are built up as 4 IF-interconnected Zeppelin dies [21]
32-bit per link per direction
interconnecting the chips
in a crossbar fashion
by single-ended signals
with a bandwidth of 42.8 GB/s
per link in each direction.
IF: Interconnect Fabric

## Slide 203: 6.1 Intra-processor interconnects in server processors (15)
b) On-die ring interconnects in server processors -1
With higher core counts crossbar switches became more and more expensive
to implement due to the highly increasing number of switches needed.
n sources need (n/2)2 switches whereas n+m switches (n+m)/2)2 switches.
E.g. 4 cores + 4 other sources require 16 switches whereas
8 cores + 4 other sources already 36.
Accordingly, individual cores-based processors with more than 4 cores switched
typically from crossbar type interconnects to ring interconnects, as
the next Figure shows.
In their Xeon server family Intel’s first ring interconnect was implemented
in the 8-core Nehalem-EX 2S/4S/8S server processor in 2010.
We note that Intel began introducing ring interconnects even in their 4-core
client processors along with the Sandy Bridge family in 2011.

## Slide 204: 6.1 Intra-processor interconnects in server processors (16)
2006
2008
2010
2012
2014
Year
IBM/Toshiba/Sony
Cell
(8C)
Graphics/HPC
Intel
Larrabee
(16C-24C)
Graphics/HPC)
Nehalem-EX
(8C)
Servers
Sandy Bridge
(4C+GPU
DT/mobiles
and subsequent
processors up to
Broadwell-based servers
Xeon Phi
Knights Ferry
(32C)
HPC
Xeon Phi
Knights Corner
(~60C)
HPC
ARM
CCN-504
(4 core clusters)
CCN-508
(8 core clusters)
CCN-502
CCN-512
(4/12 core clusters)
Emergence of on-die ring interconnects
and subsequent
DTs and mobiles

## Slide 205: 6.1 Intra-processor interconnects in server processors (17)
b) On-die ring interconnects in server processors-2
Ring interconnects typically have two counter rotating data rings to reduce latency,
as the next Figure indicates.

## Slide 206: 6.1 Intra-processor interconnects in server processors (18)
Example 1: Ring interconnect in Intel’s 8-core Nehalem-EX 2S/4S/8S server
processor (2010) [40]

## Slide 207: 6.1 Intra-processor interconnects in server processors (19)
Example 2: Different implementations of ring interconnects in Intel’s
6C/10C/12C alternatives of Ivy Bridge-EX server processors (2013) [41]

## Slide 208: 6.1 Intra-processor interconnects in server processors (20)
Example 3: Dual ring interconnects in Intel's 18-core Haswell-EP 2S server
processor (2014) [42]

## Slide 209: 6.1 Intra-processor interconnects in server processors (21)
Ring
interconnect
Mesh
interconnect
*
c) On-die 2D mesh interconnects in server processors
Long core-to-core transfer times may limit performance, as seen in the Figure
below for ARM’s interconnects [48], this motivated the introduction of 2D mesh
interconnects.

## Slide 210: 6.1 Intra-processor interconnects in server processors (22)
Interconnection style of many and multi-core processors
On-die ring interconnect
On-die 2D mesh (2D grid) interconnect
Sony/Toshiba/IBM Cell (2006): 8 cores
Tile processor (2007): 80 cores
SCC (2010): 48 cores
Larrabee (2009). 24-32 cores (cancelled)
Xeon Phi
Knights Ferry (2010): 32 cores
Knights Corner (2012): 57-61 cores
Xeon Phi
Knights Landing (2016): up to 72 cores
Nehalem-EX (Beckton) (2010) up to 8 cores
All Sandy Bridge lines (2011) up to 8 cores
All Ivy Bridge lines (from 2012 on) up to 15 cores
to
All Broadwell lines (from 2014 on) up to 24 cores
Skylake (2015) up to 4 cores
Skylake-X (HED) (2017) up to 18 cores
Skylake-SP (2017) up to 28 cores
Intel
ARM CCN504 (2012) to CCN512 (2014) Interconn.
IBM
POWER9 (2017) (Up to 24 cores)
CMN6xx Interconn. (2016) (up to 128 cores)
Move from on-die ring interconnects to on-die 2D mesh interconnects

## Slide 211: 6.1 Intra-processor interconnects in server processors (23)
Principle of the 2D mesh interconnect [43]
*
In the nodes of the 2D mesh there are routers for directing the data flow.

## Slide 212: 6.1 Intra-processor interconnects in server processors (24)
Example 1: Broadwell-EX's ring interconnect vs. Skylake-SP's 2D mesh
interconnect [9]

## Slide 213: 6.1 Intra-processor interconnects in server processors (25)
Example 2: 2D mesh interconnect of the 28-core 2S Skylake-SP (2017) [38]

## Slide 214
6.2 Inter-processor interconnects in 2S server processors
Notes: 214

## Slide 215: 6.2 Inter-processor interconnects in 2S server processors (1)
Processor interconnects in
2S SMP server platforms
Inter-processor interconnects in 2S server processors
Processor interconnects
in 2S NUMA server platforms
Inter-processor processor interconnects in 2S server platforms
There is no direct interconnection between the
processors, both processors are connected
to the MCH via the FSB (Front Side Bus) bus.
The FSB bus is a parallel, 8 Byte data width,
QDR, up to 400 MHz clock, voltage ref. signaling
QPI
QPI
IOH
ESI
QPI
Memory
DIMMs
Processor 1
Processpr 2
IOH
HI 1.5
Memory
DIMMs
Examples
Memory
DIMMs
Processors are interconnected via a
fast serial bus (QPI in the drawing).
The fast serial bus is a unidirectional
point-to-point link, 2 Byte data width,
DDR data rate, differential signaling
PCH
FSB
Processor 1
Processor 2
MCH

## Slide 216: 6.2 Inter-processor interconnects in 2S server processors (2)
HT | Base clock | Platforms (first implemented in) | Data rate (up to) (in each dir.) | Year
HT 1.0 | 0.8 GHz | K8-based mobile Athlon 64/Opteron | 3.2 GB/s | 2003
HT 2.0 | 1.0 GHz | K8-based Athlon 64 desktop | 4. GB/s | 2004
HT 3.0 | 2.6 GHz | K10.5-based Phenom X4 desktop | 8.0 GB/s | 2007
HT 3.1 | 3.2 GHz | K10.5-based Magny Course server | 12.8 GB/s | 2010
QPI | Base clock | Platforms | Data rate (up to) (in each dir.) | Year
QPI | 3.2 GHz | Nehalem (server/desktop) | 12.8 GB/s | 2008
QPI 1.1 | 4.0 GHz | Sandy Bridge EN/EP Ivy Bridge-EN/EP/EX Westmere EN/EP/EX | 16.0 GB/s | 2010-14
QPI 1.1 | 4.8 GHz | Haswell EN/EP Broadwell EN/EP | 15.2 GB/s | 2014-16
UPI | Base clock | Platforms | Data rate (up to) (in each dir.) | Year
UPI | 5.2 GHz | Skylake-SP | 20.8 GB/s | 2017
Serial links
Unidirectional point-to-point links, 2 Byte data width, DDR data rate, differential signaling
Fastest FSB
Parallel, 8 Byte data width, QDR, up to 400 MHz clock, voltage ref. signaling 12.8 GB/s data rate
Key specifications of the FSB and widely used fast serial buses

## Slide 217: 6.2 Inter-processor interconnects in 2S server processors (3)
LVDS: Low Voltage Differential Signaling LVTTL: Low Voltage TTL
(D)RSL: (Differential) Rambus Signaling Level SSTL: Stub Series Terminated Logic VCM: Common Mode Voltage VREF: Reference Voltage
VMSE: Voltage Mode Single Ended FB-DIMM: Fully Buffered DIMM
FSB: Front Side Bus SMI: Scalable Memory Interface
LVTTL (3.3 V)
FPM/EDO
SDRAM
HI 1.5
TTL (5 V)
FPM/EDO
SSTL
SSTL2 (DDR)
SSTL1.8 (DDR2)
SSTL1.5 (DDR3)
SSTL1.2 (DDR4)
RSL (RDRAM)
FSB
VMSE (SMI2)
LVDS
PCIe
QPI, UPI, DMI, ESI
HT
FB-DIMMs
DRSL
XDR (data),
IMI, SMI
Signaling systems used in buses
Signals
Single ended
voltage referenced
Single ended
ground referenced
Differential
t
t
VREF
t
S+
S-
VCM
Typ.voltage
swings
600-800 mV
200-300 mV
3.3-5 V
Signaling
system
used in
*

## Slide 218: 6.2 Inter-processor interconnects in 2S server processors (4)
90 nm Pentium 4
Prescott DP (2x1C)
E7520 MCH
ICH5R/ 6300ESB IOH
FSB
HI 1.5
90 nm Pentium 4
Prescott DP (2x1C)
FSB
DDR-266/333
DDR2-400
65 nm Pentium 4 Prescott DP (2x1C)/ Core 2 (2C/2*2C/4C)
Penryn (2C/2x2C)
631*ESB/ 632*ESB IOH
FSB
65 nm Pentium 4 Prescott DP (2x1C)/ Core 2 (2C/2*2C/4C)/
Penryn (2C/C)
FBDIMM
w/DDR2-533
Using first a single, then dual independent FSB buses in 2S SMP server
platforms (2004 then 2005-2007)
Xeon DP 2.8
/Paxville DP)
Xeon 5000
(Dempsey)
2x1C
Xeon 5100
(Woodcrest)
2C
Xeon 5300
(Clovertown)
2x2C
/
/
ESI
ESI: Enterprise System Interface (aka DMI).
4 PCIe lanes, 0.25 GB/s per lane (like the DMI interface,
providing 1 GB/s transfer rate in each direction)
HI 1.5 (Hub Interface 1.5)
8 bit wide, 66 MHz clock, QDR,
66 MB/s peak transfer rate
Xeon 5400
(Harpertown)
2x2C
Xeon 5200
(Harpertown)
2C
/
/
/
1333/1067 MT/s
800 MT/s
90 nm Pentium 4 Prescott DP based
2S platform for 2x1 cores
Pentium 4 Prescott DP/Core 2 based
2S platform for up to 2x2 cores
2x240 lines
~4x70 lines
5000 MCH
(Enhanced)
(Bensley 2S platform)

## Slide 219: 6.2 Inter-processor interconnects in 2S server processors (5)
Intel’s presentation of introducing dual independent FSB buses in their
Core 2 aimed Bensley 2S platform [49]
Higher bus speed was dictated by the higher performance of the Core 2 cores,
but higher bus speed did not allow sharing two cores on the same bus.
Previous Pentium 4
Prescott DP aimed
DP platform
Xeon 5000
(Dempsey)
cores
Paxville DP
(Xeon DP 2.8)
cores
Core 2 aimed
Bensley
DP platform
800 MT/s
1333/1067 MT/s
1333/1067 MT/s

## Slide 220: 6.2 Inter-processor interconnects in 2S server processors (6)
QPI
QPI
Up to DDR3-1067 for Xeon 6500/7500
Up to DDR3-1333 for Xeon E7-2800
SMB
SMB
SMB
SMB
ICH10
ESI
SMB
SMB
SMB
SMB
7500 IOH
QPI
/
Xeon E6500/7500
(Nehalem-EX)
(Becton)
Xeon E7-2800
(Westmere-EX) 2S
Nehalem-EX (8C) Westmere-EX (10C)
Nehalem-EX (8C) Westmere-EX (10C)
Using a single fast, serial bus (QPI) between Nehalem-EX/Westmere-EX
processors in 2S NUMA servers (2010/2011)
Nehalem-EX/Westmere-EX based NUMA platform (Boxboro-EX) for up to 10 cores
Up to DDR3-1067 for Xeon 6500/7500
Up to DDR3-1333 for Xeon E7-2800
SMI
SMI
PCIe2
x36
ESI (Enterprise Southbridge Interface) (aka DMI): PCIe2 x4

## Slide 221: 6.2 Inter-processor interconnects in 2S server processors (7)
QPI 1.1
DMI2
Up to DDR3-1600
SMB
SMB
SMB
SMB
Up to DDR3-1600
SMB
SMB
SMB
SMB
7500 POH
DMI2
/
Xeon E7-2800 v2
(Ivy Bridge-EX)
Xeon E7-2800 v2
(Ivy Bridge-EX)
Ivy Bridge -EX (15C)
Ivy Bridge -EX (15C)
QPI 1.1
Using dual higher speed serial buses (QPI 1.1) between Ivy Bridge
processors in 2S NUMA servers (2014)
Ivy Bridge-based NUMA platform (Brickland) for up to 15 cores
SMI2
SMI2
PCIe3
x32
PCIe3
x32
DMI2 (Direct Media Interface2): PCIe3 x4

## Slide 222: 6.2 Inter-processor interconnects in 2S server processors (8)
Remark
In the Ivy Bridge-EX processor Intel connected the PCIe directly to the processors,
this reduces the bandwidth needed between the processors and the chipset and
this is why a lower bandwidth connection to the chipset can be used (DMI2).
The DMI2 interface is the 2. generation DMI (Direct Media Interface) link that is
in fact a PCIe3 x4 link.
DMI2 provides 4 x 8.0 Gb/s = 32 Gb/s = 4 GB/s in each direction.
Previously, the DMI (aka ESI) link (PCIe2 4x provided
4 x 5 Gb/s x8/10 encoding = 16 Gb/s = 2 GB/s in each direction.
Compared to the QPI link the DMI2 link is a lower pin count link with reduced
transfer rate, as seen in the Table below.
 | No. of lines | Transfer rate in each direction
QPI link | 84 | Up to 12.8 GB/s
DMI2 link | 20 | 4 GB/s
Table: Pin counts and transfer rates of the QPI and DMI2 links

## Slide 223: 6.2 Inter-processor interconnects in 2S server processors (9)
Skylake-SP/Cascade Lake-SP based 2S platform (Purley) for up to 28C
UPIs
DMI3
Up to DDR4-2400
Up to DDR4-2400
C621/C622 PCH
DMI3
/
Xeon Silver 41xx/42xx
(Skylake-SP/
Cascade Lake-SP 2S)
Xeon Silver 41xx/42xx
(Skylake-SP/
Cascade Lake-SP 2S)
2 or 3
Skylake-SP (28C)
Cascade Lake-SP (28C)
Skylake-SP (28C)
Cascade Lake-SP (28C)
UPI: 10.4 GT/s
DMI3: 8 GB/s
(Purley
platform)
Using dual higher speed serial buses (UPI) between Skylake-SP/
Cascade Lake-SP NUMA server processors (2017/2019)

## Slide 224: 6.2 Inter-processor interconnects in 2S server processors (10)
Processor interconnects in AMD’s EPYC 2S systems [21]

## Slide 225: 6.2 Inter-processor interconnects in 2S server processors (11)
Remark
AMD’s 1. gen. Infinity Fabric interprocessor interface provides ~19 MB/s transfer
rates per direction per link, this is a bit less than the transfer rate of Intel’s UPI
(20.8 GB/s per direction per link).
On the other hand AMD has four links between two processors whereas Intel
only two or three (depending on the actual implementation).

## Slide 226
6.3 Connection of PCIe lanes to 2S server platforms
Notes: 226

## Slide 227: 6.3 Connection of PCIe lanes to 2S server platforms (1)
Connecting PCIe lanes to server platforms
Let’s consider two examples for connecting PCIe lanes to server platforms in the next
Figure.
Attaching PCIe lanes in Intel’s
Nehalem/Westmere-based 2S platforms
(Tylersburg platform, 2009-2010) []
Attaching PCIe lanes in Intel’s
Sandy Bridge-based 2S platforms
(Romley-EP platform, 2012) []
Next, we discuss the point, how attaching PCIe lanes to 2S servwe platforms evolved.

## Slide 228: 6.3 Connection of PCIe lanes to 2S server platforms (2)
Platform | Core | Techn. | Date of Intro. | High-end multicore 2S server lines | Core count | FSB/QPI (up to) | IF to chipset | PCIe
 | Pentium 4 DP Presc. | 90 nm | 6/2004 | 90 nm Nocona | 1C | 2xFSB 800 MT/s | HI1.5 (266 MB/s) | 24xPCIe (on MCH)
 | Pentium 4 Presc. | 90 nm | 10/2005 | Xeon DP 2.8 (Paxville DP) | 2x1C | 2xFSB 800MT/s | HI1.5 (266 MB/s) | 24xPCIe (on MCH)
Bensley | Pentium 4 Presc. | 65 nm | 5/2006 | Xeon 50xx (Dempsey) | 2x1C | 2xFSB 1066 MT/s | ESI (4xPCIe) | 24xPCIe on MCH
 | Core2 | 65 nm | 6/2006 | Xeon 51xx (Woodcrest) | 2C | 2xFSB 1333 MT/s |  | 
 | Core2 | 65 nm | 11/2006 | Xeon 53xx (Clowertown) | 2x2C | 2xFSB 1066 MT/s |  | 
 | Penryn | 45 nm | 11/2007 | Xeon 54xx (Harpertown) | 2x2C | 2xFSB1033 MT/s |  | 
Connecting PCIe lanes to server platforms
Interconnection links of Intel’s high-end multicore 2S SMP server processors
Remark: Intel’s client processors provide typically 16 PCIe lanes of the actual gen.

## Slide 229: 6.3 Connection of PCIe lanes to 2S server platforms (3)
Platform | Core | Techn. | Date of Intro. | High-end multicore 2S server lines | Core count | FSB/QPI (up to) | IF to chipset | PCIe
Tylersburg | Nehalem | 45 nm | 3/2009 | Xeon 55xx (Nehalem –EP) Gainestown) | 4C | 2xQPI 1.0 (6.3 GT/s) | QPI 1.0 (6.4 GB/s) | 36x PCIe 2.0 (on MCH)
 | Westmere | 32 nm | 3/2010 | Xeon 56xx (Westmere-EP) | 6C |  |  | 
Boxboro-EX | Nehalem | 45 nm | 3/2010 | Xeon 65xx Nehalem-EX) | 8C | 4xQPI 1.0 (6.4 GT/s) | 2xQPI 1.0 (6.4 GT/s) | 36x PCIe 2.0 (on MCH)
 | Westmere | 32 nm | 4/2011 | Xeon E7-28xx (Westmere-EX) | 10C |  |  | 
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-28xx v2 (Ivy Bridge-EX) | 15C | 3xQPI 1.1 (8 GT/s) | DMI2 x4 (4xPCIe 2.0) (2 GB/s Perdir.) | 32x PCIe 3.0 (on proc.)
Grantley | Haswell | 22 nm | 9/2014 | E5-26xx v3 (Haswell-EP) | 18C | 2xQPI 1.1 (8 GT/s) | DMI2 x4 (4xPCIe 2.0) (2 GB/s Per dir.) | 40x PCIe 3.0 (on proc.)
 | Broadwell | 14 nm | 4/2016 | E5-26xx v4 (Broadwell-EP) | 22C |  |  | 
Purley | Skylake | 14 nm | 7/2017 | Silver 41xx (Skylake-SP) | 12C | 2x UPI (9.6 GT/s) | DMI3 x4 (4xPCIe 3.0) (4 GB/s per dir.) | 44/48x PCIe 3.0 (on proc.)
 | Cascade Lake | 14 | 4/2019 | Silver 42xx Cascade Lake-SP | 16C | 2x UPI (10.4 GT/s) |  | 
?? | Cascade Lake | 14 | 4/2019 | Platinum 92xx Cascade Lake-AP | 2x28C | na. | na. | na.
Interconnection links of Intel’s high-end multicore 2S NUMA server processors

## Slide 230: 6.3 Connection of PCIe lanes to 2S server platforms (4)
Evolution of connecting PCIe lanes in Intel’s high-end 2S servers platforms
Implemented PCIe generation
Where to connect PCIe lanes
PCIe lanes
on the NB
PCIe lanes
on the processor
24 PCIe 1.0 lanes
36 PCIe 2.0 lanes
32 PCIe 3.0 lanes
44/48 PCIe 3.0 lanes
2004-2007
2009-2010
20014
2017
The next Figure summmarizes the overall evolution of implementing PCIe lanes
to a client platform.
*
40 PCIe 3.0 lanes
20014-2016

## Slide 231: 6.3 Connection of PCIe lanes to 2S server platforms (5)
PCI Express version | Intro- duced | Line code | Transfer rate in each direction | Data rate in each direction |  |  |  | 
 |  |  |  | ×1 | ×2 | ×4 | ×8 | ×16
1.0 | 2003 | 8b/10b | 2.5 GT/s | 250 MB/s | 0.50 GB/s | 1.0 GB/s | 2.0 GB/s | 4.0 GB/s
2.0 | 2007 | 8b/10b | 5.0 GT/s | 500 MB/s | 1.0 GB/s | 2.0 GB/s | 4.0 GB/s | 8.0 GB/s
3.0 | 2010 | 128b/130b | 8.0 GT/s | 984.6 MB/s | 1.97 GB/s | 3.94 GB/s | 7.88 GB/s | 15.8 GB/s
4.0 | 2017 | 128b/130b | 16.0 GT/s | 1969 MB/s | 3.94 GB/s | 7.88 GB/s | 15.75 GB/s | 31.5 GB/s
5.0 | 2019 | 128b/130b | 32.0 GT/s[ | 3938 MB/s | 7.88 GB/s | 15.75 GB/s | 31.51 GB/s | 63.0 GB/s
Main features of subsequent PCIe generations []

## Slide 232: 6.3 Connection of PCIe lanes to 2S server platforms (6)
PCIe 3.0
lanes
PCIe 2.0
lanes
Implemented PCIe generation
PCIe 1.0
lanes
Intel’s 2S server lines
PCIe lanes
on the NB
PCIe lanes
on the processor
PCIe lanes
on the NB
PCIe lanes
on the processor
PCIe 4.0
lanes
AMD’s 2S server lines
90 nm Nocona (2004)
Xeon DP 2.8 (2005)
with E7520 NB
Xeon 50xx-54xx (2006-07)
with 5000 MCH
Xeon 55xx (2009)
(Nehalem-EP)
Xeon 56xx (2010)
with 55xx NB
E7-2800 v2 (2014)
(Ivy Bridge-EX)
to
Silver 42xx (2019)
(Cascade Lake-SP)
K10.5 Shanghai (2008)
with SR5690 NB
Fam. 15h (Bulldozer)
(2011) with RX980 NB
Fam. 15h Piledriver
(2012) with SR5690
Zen-based lines (2017)
Zen+-based (2018)
Zen 2-based lines (2019)
Evolution of PCIe lanes in Intel’s and AMD’s server processors – the facts
K8 Hammer (2005)
with nVIdia nForce 2200
K10 with (2008)
with nVidia nForce 3600

## Slide 233: 6.3 Connection of PCIe lanes to 2S server platforms (7)
Consequences of attaching PCIe lanes immediately to the processor
rather than to the NB -1
There are two main consequences, as follows:
a) Three-chip platforms can now be replaced by two chip platforms and
b) The previous high BW processor-NB link can be replaced by a significantly
lower bandwidth processor-PCH/FCH link.
*

## Slide 234: 6.3 Connection of PCIe lanes to 2S server platforms (8)
a) Replacing three-chip platforms by two chip platforms
When connecting PCIe lanes directly to the processor, the NB has less tasks
to perform than before, thus the “reduced-function” NB and the SB can now
easily be integrated into a single chip.
The integrated chip is called PCH (Peripheral Control Hub) by Intel or FCH
(Fusion Control Hub) by AMD, as shown next for Intel’s 2S server processors.
*

## Slide 235: 6.3 Connection of PCIe lanes to 2S server platforms (9)
QPI
QPI
Up to DDR3-1067 for Xeon 6500/7500
Up to DDR3-1333 for Xeon E7-2800
SMB
SMB
SMB
SMB
ICH10
ESI
SMB
SMB
SMB
SMB
7500 IOH
QPI
/
Xeon 6500/7500
(Nehalem-EX)
(Becton)
Xeon E7-2800
(Westmere-EX) 2S
Nehalem-EX (8C) Westmere-EX (10C)
Nehalem-EX (8C) Westmere-EX (10C)
QPI 1.1
DMI2
Up to DDR3-1600
SMB
SMB
SMB
SMB
Up to DDR3-1600
SMB
SMB
SMB
SMB
C602 PCH
DMI2
/
Xeon E7-2800 v2
(Ivy Bridge-EX 2S)
Xeon E7-2800 v2
(Ivy Bridge-EX 2S
Ivy Bridge -EX (15C)
Ivy Bridge -EX (15C)
QPI 1.1
Nehalem-EX/Westmere-EX based 2S platform for up to 10C (2010)
Ivy Bridge based 2S platform for up to 15C (2014)
Up to DDR3-1067 for Xeon 6500/7500
Up to DDR3-1333 for Xeon E7-2800
SMI
SMI
SMI2
SMI2
Connecting PCIe lanes directly to the processors rather than to the IOH
in Intel’s Ivy Bridge-EX-based 2S platform
(Boxboro 2S platform)
(Brickland 2S platform)
32x
PCIe2
32x
PCIe 3.0
32x
PCIe 3.0
DMI2: 4x PCIe2

## Slide 236: 6.3 Connection of PCIe lanes to 2S server platforms (10)
When PCIe lanes are connected directly to the processor, the PCIe communication
bypasses the new control hub (PCH/FCH), consequently less bandwidth
is needed now between the processor and the new control hub.
Consequently, the previously used high bandwidth QPI/HT bus can be replaced
by an interface with smaller bandwidth.
This interface usuallly consists of four 2nd or 3rd generation PCIe lanes termed
e.g. by Intel as DMI or UMI, as shown subsequently.
*
b) Replacing the previous high BW processor-NB link by a significantly lower
bandwidth PCH/FCH link

## Slide 237: 6.3 Connection of PCIe lanes to 2S server platforms (11)
QPI | Base clock | Platforms | Data rate (up to) (in each dir.) | Year
QPI | 3.2 GHz | Nehalem (server/desktop) | 12.8 GB/s | 2008
QPI 1.1 | 4.0 GHz | Sandy Bridge EN/EP Ivy Bridge-EN/EP/EX Westmere EN/EP/EX | 16.0 GB/s | 2010-14
QPI 1.1 | 4.8 GHz | Haswell EN/EP/EX Broadwell EN/EP/EX | 15.2 GB/s | 2014-16
UPI | Base clock | Platforms | Data rate (up to) (in each dir.) | Year
UPI | 5.2 GHz | Skylake-SP | 20.8 GB/s | 2017
Contrasting the QPI with the FSB and other serial buses
PCIe generation | Introduced | Line code | Transfer rate In each direction | Data rate in each direction
2.0 | 2007 | 8b/10b | 5.0 GT/s | 2.0 GB/s
3.0 | 2010 | 128b/130b | 8GT/sr | 3.94 GB/s

## Slide 238: 6.3 Connection of PCIe lanes to 2S server platforms (12)
QPI
QPI
Up to DDR3-1067 for Xeon 6500/7500
Up to DDR3-1333 for Xeon E7-2800
SMB
SMB
SMB
SMB
ICH10
ESI
SMB
SMB
SMB
SMB
7500 IOH
QPI
/
Xeon 6500/7500
(Nehalem-EX)
(Becton)
Xeon E7-2800
(Westmere-EX) 2S
Nehalem-EX (8C) Westmere-EX (10C)
Nehalem-EX (8C) Westmere-EX (10C)
QPI 1.1
DMI2
Up to DDR3-1600
SMB
SMB
SMB
SMB
Up to DDR3-1600
SMB
SMB
SMB
SMB
C602 PCH
DMI2
/
Xeon E7-2800 v2
(Ivy Bridge-EX 2S)
Xeon E7-2800 v2
(Ivy Bridge-EX 2S
Ivy Bridge -EX (15C)
Ivy Bridge -EX (15C)
QPI 1.1
Nehalem-EX/Westmere-EX based 2S platform for up to 10C (2010)
Ivy Bridge based 2S platform for up to 15C (2014)
Up to DDR3-1067 for Xeon 6500/7500
Up to DDR3-1333 for Xeon E7-2800
SMI
SMI
SMI2
SMI2
Replacing the high-bandwidth processor-NB link (QPI) by the lower bandwith
DMI2 interface (4xPCIe2) in Intel’s Ivy Bridge-EX-based 2S platform
(Boxboro 2S platform)
(Brickland 2S platform)
32x
PCIe2
32x
PCIe 3.0
32x
PCIe 3.0
DMI2: 4x PCIe2

## Slide 239: 6.3 Connection of PCIe lanes to 2S server platforms (13)
Example: Connecting PCIe3 links
to the processor and using
DMI2 links to attach the PCH
in Intel’s Ivy Bridge-EX
based platforms [14]

## Slide 240: 6.3 Connection of PCIe lanes to 2S server platforms (14)
Example: Connecting PCIe3 lanes to the processor in AMD’s EPYC based platforms [44]
Remark: In EPYC the PCH
is integrated

## Slide 241
7. References
Notes: 241

## Slide 242
[1]: Intel Secretly Firefighting a Major CPU Bug Affecting Datacenters?, TechPowerUp, Jan. 3 2018,
https://www.techpowerup.com/240174/intel-secretly-firefighting-a-major-cpu-bug-
affecting-datacenters#g240174
References (1)
[3]: De Gelas J., The Intel Xeon E7-8800 v3 Review: The POWER8 Killer?, AnandTech,
May 8 2015, http://www.anandtech.com/show/9193/the-xeon-e78800-v3-review
[4]: AMD, Intel server market trends, XbitLabs, Aug. 2011,
http://www.xbitlabs.com/picture/?src=/images/news/2011-08/amd_intc_server_mkt_
trends.png
[5]: Hibben M., Will IBM Sell Its Mainframe Business? Seeking Alpha, Jul. 20, 2016
http://seekingalpha.com/article/3989959-will-ibm-sell-mainframe-business?auth_
param=djq9a:1bovpmu:2be6695ecca2e22ac60039ce2a123ea7
[6]: Molka D., Hackenberg D., Schöne R., Müller M. S., Memory Performance and Cache
Coherency Effects on an Intel Nehalem multiprocessor System, Proc. 18th Int. Conf.
on Parallel Architectures and Compilation, Techniques, PACT 2009,
http://doi.ieeecomputersociety.org/10.1109/PACT.2009.22
[2]: A New Day for the Datacenter, Presentation at AMD Financial Analyst Day, May 16 2017,
http://ir.amd.com/phoenix.zhtml?c=74093&p=irol-analystday
[7]: Danowitz A. & al. CPU DB: Recording Microprocessor History, Communications of the
ACM, Vol. 55 No. 4, Pages 55-63
[8]: Esmer I., Ivybridge Server Architecture: A Converged Server, Aug. 2014, Hot Chips 2014,
http://www.hotchips.org/wp-content/uploads/hc_archives/hc26/HC26-12-day2-epub/
HC26.12-8-Big-Iron-Servers-epub/HC26.13.832-IvyBridge-Esmer-Intel-IVB%20Server%
20Hotchips2014.pdf

## Slide 243
[9]: Kumar A., Trivedi M., Intel Xeon Scalable Processor Architecture Deep Dive, June 12 2017,
https://www.primeline-solutions.de/files/intel-xeon-scalable-architecture-deep-dive_1.pdf
References (2)
[11]: EPYC – AMD, Wikichip, https://en.wikichip.org/wiki/amd/epyc
[12]: https://en.wikipedia.org/wiki/RC_circuit
[14]: Supermicro Motherboards, MNL-1594X6QT8, User Manual,
https://www.supermicro.com/manuals/motherboard/C606_602/MNL-1594.pdf
[10]: De Gelas J., Cutress I., Sizing Up Servers: Intel's Skylake-SP Xeon versus AMD's EPYC
7000 - The Server CPU Battle of the Decade?, AnandTech, July 11 2017,
http://www.anandtech.com/show/11544/intel-skylake-ep-vs-amd-epyc-7000-cpu-battle-
of-the-decade/7
[15]: Haas J. & Vogt P., Fully buffered DIMM Technology Moves Enterprise Platforms to the
Next Level, Technology Intel Magazine, March 2005, pp. 1-7
[16]: Radhakrishnan S., Chinthamani S., Cheng K., The Blackford Northbridge Chipset for the
Intel 5000, IEEE Micro, Vol. 27, Issue 2, March-April 2007, pp. 22-33
[13]: Kennedy P., Intel Xeon Scalable Processor Family Platform Level Overview, July 11 2017,
STH, https://www.servethehome.com/intel-xeon-scalable-processor-family-platform-
level-overview/
[17]: Intel 7500/7510/7512 Scalable Memory Buffer, Datasheet, April 2011,
https://www.intel.com/content/dam/doc/datasheet/7500-7510-7512-scalable-memory-
buffer-datasheet.pdf

## Slide 244
[18]: Supermicro, X10DRC/i-LN4+/-T4+ Motherboard User’s Manual, 2018,
https://www.supermicro.com/manuals/motherboard/C600/MNL-1560.pdf
References (3)
[20]: Alcorn P., Intel Plays Defense: Inside Its EPYC Slide Deck, Tom’s Hardware, July 17 2017,
http://www.tomshardware.com/reviews/intel-amd-die-fabric-slides,5125-2.html
[21]: Cutress I., AMD's Future in Servers: New 7000-Series CPUs Launched and EPYC Analysis,
AnandTech, June 20 2017, http://www.anandtech.com/show/11551/amds-future-in-
servers-new-7000-series-cpus-launched-and-epyc-analysis/2
[23]: Teich P., The New Server Economies Of Scale For AMD, The Next Platform, July 13 2017,
https://www.nextplatform.com/2017/07/13/new-server-economies-scale-amd/
[19]: Supermicro, X11DGQ User's Manual, 2019
https://www.supermicro.com/manuals/motherboard/C620/MNL-2016.pdf
[24]: Beck, N. & al., "Zeppelin": An SoC for Multichip Architectures, ISSCC 2018, Febr. 12 2018,
Presentation slides,
https://www.slideshare.net/AMD/isscc-2018-zeppelin-an-soc-for-multichip-architectures
[25]: Infinity Fabric (IF) - AMD, https://en.wikichip.org/wiki/amd/infinity_fabric
[22]: Kennedy P., AMD EPYC Infinity Fabric Update and MCM Cost Savings, STH, Aug. 22 2017,
https://www.servethehome.com/amd-epyc-infinity-fabric-update-mcm-cost-savings/
[26]: Alcorn P., Intel Presents Its AMD EPYC Server Test Results, Tom’s Hardware, Nov. 27 2017,
https://www.tomshardware.com/news/amd-intel-epyc-xeon-benchmarks,35993.html

## Slide 245
[27]: Teich P., The Heart Of AMD’s EPYC Comeback Is Infinity Fabric, The Next Platform, July 12 2017,
https://www.nextplatform.com/2017/07/12/heart-amds-epyc-comeback-infinity-fabric/
References (4)
[29]: H11DSI-NT Users’s Manual, Supermicro, 2017
[30]: R281-Z91, https://b2b.gigabyte.com/Rack-Server/R281-Z91-rev-100#ov
[32]: Mujtaba H., AMD EPYC Rome Officially Launched: 7nm High-Performance Server CPUs
With More Cores, Higher Frequencies – Best-In-Class Performance, Efficiency, and Value,
WCFTech, Aug. 7, 2019, https://wccftech.com/amd-epyc-rome-7nm-server-cpu-official-
launch-64-core-128-thread-128-pcie-gen4/
[28]: Kingsley-Hughes A., AMD EPYC: What you need to know, ZD Net, June 21 2017,
http://www.zdnet.com/article/amd-epyc-what-you-need-to-know/
[33]: Prickett T., AMD’s Long Road From Naples To Milan Centers On Rome, TheNextPlatform,
Nov. 6, 2018, https://www.nextplatform.com/2018/11/06/amds-long-road-from-naples-
to-milan-centers-on-rome/
[34]: De Gelas J., AMD Rome Second Generation EPYC Review: 2x 64-core Benchmarked,
AnandTech, Aug. 7, 2019,
https://www.anandtech.com/show/14694/amd-rome-epyc-2nd-gen/8
[31]: Tayal P., AMD EPYC Rome Cheaper, More Powerful than Intel CPU, Market Realist,
Aug. 23 2019,
https://marketrealist.com/2019/08/amd-epyc-rome-cheaper-more-powerful-than-intel/

## Slide 246
[35]: Larabel M., AMD EPYC 7002 Series Unveiled With Primed Linux Support & Strong Server
Performance, Phoronix, Aug. 9, 2019,
https://www.phoronix.com/scan.php?page=article&item=amd-linux-epyc-7002&num=1
References (5)
[36]: Prickett T., Intel To Challenge AMD With 48 Core “Cascade Lake” Xeon App, TheNextPlatform,
Nov. 5, 2018, https://www.nextplatform.com/2018/11/05/intel-to-challenge-amd-with-
48-core-cascade-lake-xeon-ap/
[38]: Chiappetta M., Intel Xeon Scalable Debuts: Dual Xeon Platinum 8176 With 112 Threads
Tested, Hot Hardware, July 11 2017,
https://hothardware.com/reviews/intel-xeon-scalable-processor-family-review
[39]: Shimpi A.L., Intel's Sandy Bridge Architecture Exposed, AnandTech, Sept. 14 2010,
https://www.anandtech.com/show/3922/intels-sandy-bridge-architecture-exposed/4
[40]: Kottapalli S., Baxter J., Nehalem-EX CPU Architecture, Hot Chips 2009,
https://www.hotchips.org/wp-content/uploads/hc_archives/hc21/2_mon/HC21.24.100.
ServerSystemsI-Epub/HC21.24.122-Kottapalli-Intel-NHM-EX.pdf
[37]: Larabel M., POWER9 & ARM Performance Against Intel Xeon Cascadelake + AMD EPYC
Rome, Phoronix, Aug. 19, 2019,
https://www.phoronix.com/scan.php?page=article&item=rome-power9-arm&num=4
[41]: De Gelas J., Intel's Xeon E5-2600 V2: 12-core Ivy Bridge EP for Servers, AnandTech,
Sept. 17 2013, http://www.anandtech.com/show/7285/intel-xeon-e5-2600-v2-12-core-
ivy-bridge-ep

## Slide 247
[42]: Morgan T. P., Intel Puts More Compute Behind Xeon E7 Big Memory, The Platform,
May 5 2015, http://www.theplatform.net/2015/05/05/intel-puts-more-compute-behind-
xeon-e7-big-memory/
References (5)
[43]: Intel Xeon Scalable Platform, Newsroom, 2017,
https://newsroom.intel.com/newsroom/wp-content/uploads/sites/11/2017/07/intel-xeon-
scalable-processors-overview.pdf
[45]: Intel 64 and IA-32 Architectures Optimization Reference Manual, June 2016,
https://www.intel.com/content/dam/www/public/us/en/documents/manuals/64-ia-32-
architectures-optimization-manual.pdf
[44]: Supermicro, H11DSi / H11DSi-NT User's Manual, 2018,
https://www.supermicro.com/manuals/motherboard/EPYC7000/MNL-2027.pdf
[46]: Sima D., The Square Root Rule for Scaling Memory Channels in Servers, in Recent Advances
in Intelligent Engineering, pp. 39-63, Springer, January 2019,
https://link.springer.com/chapter/10.1007%2F978-3-030-14350-3_3
[47]: IBM Blue Gene, Wikipedia, visited on the 20. 10. 2019,
https://en.wikipedia.org/wiki/IBM_Blue_Gene
[48]: Parris N., Boost SoC performance from edge to cloud ARM CoreLink System IP, ARM,
Nov. 2016, http://www.armtechforum.com.cn/attached/article/2016ATS_C1_Neil_Parris
20161206151154.pdf
[49]: Inkley B., Tetrick S.: Intel Multi-core Architecture and Implementations, IDF, Session
MATS002, March 7 2006

## Slide 248
https://wccftech.com/amd-zen-3-epyc-milan-and-zen-4-epyc-genoa-server-cpu-detailed/