10. Rendszerarchitektúrák

Busses:

Figure 1.: Busses

Figure 2.: Main features of the system-bus

Figure 3.: General purpose peripheral busses

Figure 4.: Early implementations of the ISA-bus

Figure 5.. Dedicated busses

Figure 6.: Storage interfaces

Figure 7.: IDE/ATA

Figure 8.: Basic transfer modes of the IDE/ATA standards

Figure 9.: SCSI

Figure 10.: AGP

Figure 11.: AC ’97

Figure 12.: AC ’97

Figure 13.: Implementation of the AC ’97

DRAMs:

Figure 14.: DRAMs

Figure 15.: Memory modules

Figure 16.: Serial Presence Detect (SPD)

Figure 17.: Packaging of memory modules

Figure 18.: DIMMs

Figure 19.: The JEDEC Serial Presence Direct (SPD) standard for DIMMs

Figure 20.: PC100 module identification

CHIPSETS:

Figure 21.: Overview of the Intel chipsets

Figure 22.: Chipsets I.: Supported DRAM features

Figure 23.: Chipsets II.: Supported I/O-features

Figure 9.4: Main features of Intel’s 845xx family of chipsets

Figure 9.10: Intel’s chipsets designed for P4-based value and desktop PCs

Figure 9.14: Bus innovations introduced into Intel’s P4 chipsets

Figure 9.16: The evolution of chipsets intended primarily for P4-based value/mainstream desktops

Table 9.30: Main features of the FSB and SDRAM interface

Table 9.31: Main features of MCH/ICH interfaces of Intel’s P4-based chipsets

Table 9.32: Main features of high speed MCH interfaces of Intel’s P4-based chipsets

Table 9.33: Peak bandwidth values and sustained data rates of peripheral buses

Figure 9.34: Peak bandwidth values (Mbyte/s) in a typical value/desktop motherboard based on Intel’s 865xx family of chipsets

Figure 9.35: Peak bandwidth values (Mbyte/s) in a typical value/desktop motherboard based on Intel’s 915xx family of chipsets

System architecture:

Figure 24.: Evolution of the system architecture

Figure 25.: ISA-bus based system architecture (Used typically in 08088/80286/80386-based PCs)

Figure 26.: Straight forward PCI-based system architecture (Used typically in 486 and early Pentium-based PCs along with Intel 420 and early 430 chipsets)

Figure 27.: PCI-based system architecture with IDE/ATA and USB ports (Used typically in mature Pentium-based PCs with mature Intel 430 chipsets)

Figure 28.: PCI-based system architecture with AGP, IDE/ATA and USB ports(Used typically in early PentiumII and PentiumIII-based PCs with Intel 440XX chipsets)

Figure 29.: Ports-based system architecture (Used typically in mature PentiumII- and PentiumIII-based systems with Intel 8X0 chipsets Excluding the 810, which includes an integrated display controller rather than an AGP port)

Figure 30.:Mainstream evolution of the system architecture

Caches:

Figure 31.: Evolution of cache architectures

Figure 32.: Main features of AMD K6 and Athlon K7 cores

Figure 33.: Main features of Intel’s Pentium II/III and Pentium 4 cores

Figure 34.: Main parameters of L1 caches

Figure 35.:

- External L1-cache

- On-die unified L1-cache with optional (external, unified) L2-cache

- On-die split L1-cache with optional (external, unified) L2-cache

- Direct coupled L2-cache

- On-die L2-cache

- On-die L2-cache with an external front-end L3-cache

- On-die L2-cache with a direct coupled L3-cache

Figure 1.: Busses

Figure 2.: Main features of the system-bus

Figure 3.: General purpose peripheral busses

Figure 4.: Early implementations of the ISA-bus

Figure 5.. Dedicated busses

Figure 6.: Storage interfaces

Figure 7.: IDE/ATA

Figure 8.: Basic transfer modes of the IDE/ATA standards

Figure 9.: SCSI

Figure 10.: AGP

Figure 11.: AC ’97

Figure 12.: AC ’97

Figure 13.: Implementation of the AC ’97

Figure 14.: DRAMs

Figure 15.: Memory modules

Figure 16.: Serial Presence Detect (SPD)

Figure 17.: Packaging of memory modules

Figure 18.: DIMMs

Figure 19.: The JEDEC Serial Presence Direct (SPD) standard for DIMMs

Figure 20.: PC100 module identification

Figure 21.: Overview of the Intel chipsets

Figure 22.: Chipsets I.: Supported DRAM features

Figure 23.: Chipsets II.: Supported I/O-features

Figure 9.4: Main features of Intel’s 845xx family of chipsets

Figure 9.10: Intel’s chipsets designed for P4-based value and desktop PCs

Figure 9.14: Bus innovations introduced into Intel’s P4 chipsets

Figure 9.16: The evolution of chipsets intended primarily for P4-based value/mainstream desktops

Table 9.30: Main features of the FSB and SDRAM interface

Table 9.31: Main features of MCH/ICH interfaces of Intel’s P4-based chipsets

Table 9.32: Main features of high speed MCH interfaces of Intel’s P4-based chipsets

Table 9.33: Peak bandwidth values and sustained data rates of peripheral buses

Figure 9.34: Peak bandwidth values (Mbyte/s) in a typical value/desktop motherboard based on Intel’s 865xx family of chipsets

Figure 9.35: Peak bandwidth values (Mbyte/s) in a typical value/desktop motherboard based on Intel’s 915xx family of chipsets

Figure 24.: Evolution of the system architecture

# Figure 25.: ISA-bus based system architecture

(Used typically in 8088/80286/80386-based PCs)

# Figure 26.: Straight forward PCI-based system architecture

# (Used typically in 486 and early Pentium-based PCs

# along with Intel 420 and early 430 chipsets)

# Figure 27.: PCI-based system architecture with IDE/ATA and USB ports

# (Used typically in mature Pentium-based PCs with mature Intel 430 chipsets)

# IDE port:     First on the 430FX (Triton, 1995)

# ATA/33:	First on the 430TX (1997)

# USB:   	First on the 430VX (Triton III, 1996)

# Figure 28.: PCI-based system architecture with AGP, IDE/ATA and USB ports

(Used typically in early PentiumII and PentiumIII-based PCs with Intel 440XX chipsets)

# Figure 29.: Ports-based system architecture

(Used typically in mature PentiumII- and PentiumIII-based systems with Intel 8X0 chipsets

Excluding the 810, which includes an integrated display controller rather than an AGP port)

Figure 30.: Mainstream evolution of the system architecture

Figure 31.: Evolution of cache architectures

Figure 32.: Main features of AMD K6 and Athlon K7 cores

Figure 33.: Main features of Intel’s Pentium II/III and Pentium 4 cores

Figure 34.: Main parameters of L1 caches

External L1-cache

# Examples: Intel 386 based systems with optional L1-cache

# On-die unified L1-cache with optional (external, unified) L2-cache

# Examples: Intel 486-based systems

# On-die split L1-cache with optional (external, unified) L2-cache

# Exmples: Intel Pentium, AMD K5, K6, K6-2 based systems

# Direct coupled L2-cache

Examples: Intel Pentium Pro, Pentium II (expect Mendocino), Pentium III (0.25μ technology) and AMD Athlon (K7, K75 cores) based systems

# On-die L2-cache

Examples: Intel Pentium II (Mendocino core), Pentium III (0.18μ technology), Pentium4, Athlon (Thunderbird core), Athlon 4, Duron (Spitfire core)

# On-die L2-cache with an external front-end L3-cache

# Examples: Pentium 4 original design, K6-III

# On-die L2-cache with a direct coupled L3-cache

# Examples: Itanium