Dual/multi-core processors

1. Overview

Figure 1.1: Processor power density trends

Figure 1.2: Dual/multi-core processors (1)

Figure 1.3: Dual/multi-core processors (2)

Figure 1.4: Main aspects of the design space of the macro architecture of dual/multi-core processors

2. Attaching L2 caches

Figure 2.1: Main design space dimensions of laying out L2 caches for dual/multi-core processors

Figure 2.2: Allocation of L2 caches to the cores and their use by instructions and data in dual/multi-core processors

Figure 2.3: Integration of L2 caches to the processor chip in dual/multi-core processors

Figure 2.4: Examples for using private L2 caches in dual/multi-core processors

Figure 2.5: Examples for using shared L2 caches in dual/multi-core processors

3. Attaching L3 caches

Figure 3.1: Main design space dimensions of laying out L3 caches for dual/multi-core processors

Figure 3.2: Inclusion policy and allocation of L3 caches in dual/multi-core processors

Figure 3.3: Use of L3 caches in dual/multi-core processors

Figure 3.4: Exclusive cache architecture

Figure 3.5: Examples for using inclusive L3 caches in dual/multi-core processors

Figure 3.6: Examples for using exclusive L3 caches in dual/multi-core processors

Figure 3.7: Integration of L3 caches to the processor chip in dual/multi-core processors

4. Connecting memory and I/O

Figure 4.1: Main design space dimensions of laying out the I/O and memory architecture in dual/multi-core processors

Figure 4.2: Connection policy of I/O and memory in dual/multi-core processors

Figure 4.3: Examples for connecting both I/O and memory via the system bus in dual core processors

Figure 4.4: Examples for dedicated connection of I/O and memory in dual/multi-core processors

Figure 4.5: Integration of the memory controller to the processor chip in dual/multi-core processors

5. Selected implementations

Intel’s dual/multi-core processors

Figure 5.1: The move to Intel multi-core

Figure 5.2: Processor specifications of Intel’s Pentium D family

Figure 5.3: Specifications of Intel’s Pentium Processor Extrem Edition, models 840/955/965

Figure 5.4: Processor Specifications of Intel’s Yonah Duo (Core Duo) family

Figure 5.5: Future 65 nm processors (overview)

Figure 5.6: Future 45 nm processors (overview)

AMD’s Athlon 64 X2

Figure 5.7: AMD Athlon 64 X2 dual-core processor architecture

Sun’s UltraSPARC IV family

Figure 5.8: UltraSPARC IV (Jaguar)

Figure 5.9: UltraSPARC IV+ (Panther )

IBM’s POWER4/POWER5

Figure 5.10: POWER4 chip logical view

Figure 5.11: POWER4 chip

Figure 5.12: POWER4 and POWER5 system structures

Figure 1.1: Processor power density trends

Source: D. Yen: Chip Multithreading Processors Enable Reliable High Throughput Computing

http://www.irps.org/05-43rd/IRPS_Keynote_Yen.pdf

Figure 1.2: Dual/multi-core processors (1)

Figure 1.3: Dual/multi-core processors (2)

Figure 1.4 : Main aspects of the design space of the macro architecture of dual/multi-core processors

Figure 2.1: Main design space dimensions of laying out L2 caches for dual/multi-core processors

Figure 2.2: Allocation of L2 caches to the cores and their use by instructions and data in dual/multi-core processors

Figure 2.3: Integration of L2 caches to the processor chip in dual/multi-core processors

Figure 2.4: Examples for using private L2 caches in dual/multi-core processors

Figure 2.5: Examples for using shared L2 caches in dual/multi-core processors

Figure 3.1: Main design space dimensions of laying out L3 caches for dual/multi-core processors

Figure 3.2: Inclusion policy and allocation of the L3 cache in dual/multi-core processors

Figure 3.3: Use of L3 caches in dual/multi-core processors

Figure 3.4: Exclusive cache architecture

Source: Zheng, Y., Davis, B.T., Jordan, M.: “ Performance evaluation of exclusive cache hierarchies”, 
2004 IEEE International Symposium on Performance Analysis of Systems and Software (ISPASS), 2004, pp. 89-96.

Figure 3.5: Examples for using inclusive L3 caches in dual/multi-core processors

Figure 3.6: Examples for using exclusive L3 caches in dual/multi-core processors

Figure 3.7: Integration of L3 caches to the processor chip in dual/multi-core processors

Figure 4.1: Main design space dimensions of laying out the I/O and memory architecture in dual/multi-core processors

Figure 4.2: Connection policy of I/O and memory in dual/multi-core processors

Figure 4.3: Examples for connecting both I/O and memory via the system bus in dual core processors

Figure 4.4: Examples for dedicated connection of I/O and memory in dual/multi-core processors

Figure 4.5: Integration of the memory controller to the processor chip in dual/multi-core processors

Figure 5.1: The move to Intel multi-core

Source: A. Loktu: Itanium 2 for Enterprise Computing 
http://h40132.www4.hp.com/upload/se/sv/Itanium2forenterprisecomputing.pps

|  | Intel® Pentium® D Processor 950 Remove | Intel® Pentium® D Processor 940 Remove | Intel® Pentium® D Processor 930 Remove | Intel® Pentium® D Processor 920 Remove | Intel® Pentium® D Processor 840 Remove | Intel® Pentium® D Processor 830 Remove | Intel® Pentium® D Processor 820 Remove | Intel® Pentium® D Processor 805 Remove | Intel® Pentium® D Processor 960 Remove |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Processor Number Δ | 950 | 940 | 930 | 920 | 840 | 830 | 820 | 805 | 960 |
| Architecture | 65 nanometer technology | 65 nanometer technology | 65 nanometer technology | 65 nanometer technology | 90 nanometer technology | 90 nanometer technology | 90 nanometer technology | 90 nanometer technology | 65 nanometer technology |
| L2 Cache | 2x2M | 2x2M | 2x2M | 2x2M | 2x1M | 2x1M | 2x1M | 2x1M | 2x2M |
| L3 Cache | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| Clock Speed | 3.40 GHz | 3.20 GHz | 3 GHz | 2.80 GHz | 3.20 GHz | 3 GHz | 2.80 GHz | 2.66 GHz | 3.60 GHz |
| Front Side Bus Speed | 800 MHz | 800 MHz | 800 MHz | 800 MHz | 800 MHz | 800 MHz | 800 MHz | 533 MHz | 800 MHz |
| Other Intel Technologies | Execute Disable Bit°, VT±, Intel® EM64TØ, dual-core | Execute Disable Bit°, VT±, Intel® EM64TØ, dual-core | Execute Disable Bit°, VT±, Intel® EM64TØ, dual-core | Execute Disable Bit°, VT±, Intel® EM64TØ, dual-core | Execute Disable Bit°, Intel® EM64TØ, dual-core, EIST* | Execute Disable Bit°, Intel® EM64TØ, dual-core, EIST* | Execute Disable Bit°, Intel® EM64TØ, dual-core | Execute Disable Bit°, Intel® EM64TØ, dual-core | Execute Disable Bit°, VT±, Intel® EM64TØ, dual-core, EIST* |
| Package | FC-LGA | FC-LGA | FC-LGA | FC-LGA | FC-LGA | FC-LGA | FC-LGA | FC-LGA | LGA 775 |
| Chipset | Intel® 945 Express Chipset, Intel® 955X Express Chipset, Intel® 975X Express Chipset | Intel® 945 Express Chipset, Intel® 955X Express Chipset, Intel® 975X Express Chipset | Intel® 945 Express Chipset, Intel® 955X Express Chipset, Intel® 975X Express Chipset | Intel® 945 Express Chipset, Intel® 955X Express Chipset, Intel® 975X Express Chipset | Intel® 955X Express Chipset, Intel® 945G Express Chipset, Intel® 945P Express Chipset, Intel® E7230 Chipset | Intel® 955X Express Chipset, Intel® 945G Express Chipset, Intel® 945P Express Chipset, Intel® E7230 Chipset | Intel® 955X Express Chipset, Intel® 945G Express Chipset, Intel® 945P Express Chipset, Intel® E7230 Chipset | Intel® 975X Express Chipset, Intel® 945 Express Chipset, Intel® E7230 Chipset, Intel® 955X Express Chipset | Intel® 945 Express Chipset, Intel® 975X Express Chipset |

Figure 5.2: Processor specifications of Intel’s Pentium D family

Source: http://www.intel.com/products/processor/index.htm

|  | Pentium® Processor Extreme Edition 965 Remove | Pentium® Processor Extreme Edition 955 Remove | Pentium® Processor Extreme Edition 840 Remove |
| --- | --- | --- | --- |
| Processor Number Δ | 965 | 955 | 840 |
| Architecture | 65 nanometer technology | 65 nanometer technology | 90 nanometer technology |
| L2 Cache | 2x2M | 2x2M | 2x1M |
| L3 Cache | N/A | N/A | N/A |
| Clock Speed | 3.73 GHz | 3.46 GHz | 3.20 GHz |
| Front Side Bus Speed | 1066 MHz | 1066 MHz | 800 MHz |
| Other Intel Technologies | HT† Enabled, Intel® EM64TØ, VT±, Execute Disable Bit°, dual-core | HT† Enabled, Execute Disable Bit°, VT±, Intel® EM64TØ, dual-core | HT† Enabled, Execute Disable Bit°, Intel® EM64TØ, dual-core |
| Package | FC-LGA | FC-LGA | FC-LGA |
| Chipset | Intel® 975X Express Chipset | Intel® 975X Express Chipset | Intel® 955X Express Chipset |
| Memory Type | NA | Dual Channel DDR2 400/533 | Dual-Channel DDR2 |
| Boards | NA | Intel® Desktop Board D975XBX | Intel® Desktop Board D955XCS, Intel® Desktop Board D955XBK |
| Slot/Socket Type | LGA775 | LGA775 | LGA775 |
| Min-Max Voltage | 1.200 - 1.3375 | 1.25-1.40 | 1.20-1.40 |
| Pin Count | 775-land | 775-land | 775-land |
| sSpec Number | SL9AN | SL94N | SL8FK |

Figure 5.3 Specifications of Intel’s Pentium Processor Extrem Edition models 840/955/965

Source: http://www.intel.com/products/processor/index.htm

|  | Intel® Core™ Duo processor T2600 Remove | Intel® Core™ Duo processor T2500 Remove | Intel® Core™ Duo processor T2400 Remove | Intel® Core™ Duo processor T2300 Remove | Intel® Core™ Duo processor L2400 (Low Voltage) Remove | Intel® Core™ Duo processor L2300 (Low Voltage) Remove |
| --- | --- | --- | --- | --- | --- | --- |
| Processor NumberΔ | T2600 | T2500 | T2400 | T2300 | L2400 | L2300 |
| Architecture | 65-nm process technology | 65-nm process technology | 65-nm process technology | 65-nm process technology | 65-nm process technology | 65-nm process technology |
| L2 Cache | 2MB | 2MB | 2MB | 2MB | 2MB | 2MB |
| Clock Speed | 2.16 GHz | 2 GHz | 1.83 GHz | 1.66 GHz | 1.66 GHz | 1.50 GHz |
| Front Side Bus | 667 MHz | 667 MHz | 667 MHz | 667 MHz | 667 MHz | 667 MHz |
| Chipset | Mobile Intel® 945PM Chipset, Mobile Intel® 945GM Chipset | Mobile Intel® 945GM Chipset, Mobile Intel® 945PM Chipset | Mobile Intel® 945GM Chipset, Mobile Intel® 945PM Chipset | Mobile Intel® 945GM Chipset, Mobile Intel® 945PM Chipset | Mobile Intel® 945GM Chipset, Mobile Intel® 945PM Chipset | Mobile Intel® 945GM Chipset, Mobile Intel® 945PM Chipset |
| Wireless | Intel® PRO/ Wireless 3945ABG 802.11a/b/g | Intel® PRO/ Wireless 3945ABG 802.11a/b/g | Intel® PRO/ Wireless 3945ABG 802.11a/b/g | Intel® PRO/ Wireless 3945ABG 802.11a/b/g | Intel® PRO/ Wireless 3945ABG 802.11a/b/g | Intel® PRO/ Wireless 3945ABG 802.11a/b/g |

Figure 5.4: Procesor specifications of Intel’s Yonah Duo (Core Duo) family

Source: http://www.intel.com/products/processor/index.htm

| Category | Code Name | Cores | Cache | Market |
| --- | --- | --- | --- | --- |
| Desktop | Kentsfield | Dual core multi-die | 4 MB | Mid 2007 |
| Desktop | Conroe | Dual core single die | 4 MB shared | End 2006 |
| Desktop | Allendale | Dual core single die | 2 MB shared | End 2006 |
| Desktop | Cedar Mill (NetBurst/P4) | Single core | 512 kB, 1 MB, 2 MB | Early 2006 |
| Desktop | Presler (NetBurst/P4) | Dual core, dual die | 4 MB | Early 2006 |
| Desktop/Mobile | Millville | Single core | 1 MB | Early 2007 |
| Mobile | Yonah2 | Dual core, single die | 2 MB | Early 2006 |
| Mobile | Yonah1 | Single core | 1/2 MB | Mid 2006 |
| Mobile | Stealey | Single core | 512 kB | Mid 2007 |
| Mobile | Merom | Dual core, single die | 2/4 MB shared | End 2006 |
| Enterprise | Sossaman | Dual core, single die | 2 MB | Early 2006 |
| Enterprise | Woodcrest | Dual core, single die | 4 MB | Mid 2006 |
| Enterprise | Clovertown | Quad core, multi-die | 4 MB | Mid 2007 |
| Enterprise | Dempsey (NetBurst/Xeon) | Dual core, dual die | 4 MB | Mid 2006 |
| Enterprise | Tulsa | Dual core single die | 4/8/16 MB | End 2006 |
| Enterprise | Whitefield | Quad core single die | 8 MB, 16 MB shared | Early 2008 |

Figure 5.5: Future 65 nm processors (overview)

Source: P. Schmid: Top Secret Intel Processor Plans Uncovered 
www.tomshardware.com/2005/12/04/top_secret_intel_processor_plans_uncovered

|  | Codename | Cores | Cache | Market |
| --- | --- | --- | --- | --- |
| Desktop | Wolfdale | Dual core, single die | 3 MB shared | 2008 |
| Desktop | Ridgefield | Dual core single die | 6 MB shared | 2008 |
| Desktop | Yorkfield | 8 cores multi-die | 12 MB shared | 2008+ |
| Desktop | Bloomfield | Quad core, single die | - | 2008+ |
| Desktop/Mobile | Perryville | Single core | 2 MB | 2008 |
| Mobile | Penryn | Dual core single die | 3 MB, 6 MB shared | 2008 |
| Mobile | Silverthorne | - | - | 2008+ |
| Enterprise | Hapertown | 8 cores multi-die | 12 MB shared | 2008 |

Figure 5.6: Future 45 nm processors (overview)

Source: P. Schmid: Top Secret Intel Processor Plans Uncovered 
www.tomshardware.com/2005/12/04/top_secret_intel_processor_plans_uncovered

Figure 5.7: AMD Athlon 64 X2 dual-core processor architecture

Source: AMD Athlon 64 X2 Dual-Core Processor for Desktop – Key Architecture Features,

http:///www.amd.com/us-en/Processors/ProductInformation/0,,30_118_9485_13041.00.html

Figure 5.8: UltraSPARC IV (Jaguar)

Source: C. Boussard: Architecture des processeurs

http://laser.igh.cnrs.fr/IMG/pdf/SUN-CNRS-archi-cpu-3.pdf

Figure 5.9: UltraSPARC IV+ (Panther)

Source: C. Boussard: Architecture des processeurs

http://laser.igh.cnrs.fr/IMG/pdf/SUN-CNRS-archi-cpu-3.pdf

Figure 5.10: POWER4 chip logical view

Source: J.M. Tendler, S. Dodson, S. Fields, H. Le, B. Sinharoy: Power4 System Microarchitecture, IBM Server, 
Technical White Paper, October 2001

http://www-03.ibm.coom/servers/eserver/pseries/hardware/whitepapers/power4.pdf

Figure 5.11: POWER4 chip

Source: R. Kalla, B. Sinharoy, J. Tendler: Simultaneous Multi-threading Implementation in Power5 – IBM’s Next Generation POWER Microprocessor, 2003

http://www.hotchips.org/archives/hc15/3_Tue/11.ibm.pdf

Figure 5.12: POWER4 and POWER5 system structures

Source: R. Kalla, B. Sinharoy, J.M. Tendler: IBM Power5 chip: A Dual-core multithreaded Processor, 
IEEE. Micro, Vol. 24, No.2, March-April 2004, pp. 40-47.