## Slide 1
Without obstacles

## Slide 2
We start to propagate from the destination

## Slide 3
Diagonals cost more

## Slide 4
We expand to the surrounding cells.

## Slide 5
The first empty cell next to the wave

## Slide 6
Seraches for the shortest path

## Slide 7
New value = previous + cost of the step

## Slide 8
Next cell

## Slide 9
Examine the neighbours

## Slide 10
The smallest is two but the cost is three

## Slide 12
Two is the smallest from the neighbours

## Slide 13
The cost of the move is two so the next value is four

## Slide 16
Smallest + cost

## Slide 19
3+3=6

## Slide 20
Next row

## Slide 21
Examining the neighbours

## Slide 22
2+3 = 5

## Slide 24
We are searching the minimum value

## Slide 25
2+3 = 5

## Slide 28
2+2 = 4

## Slide 31
2+2 = 4

## Slide 33
Propagates a new wave to the next cells

## Slide 34
The first empty cell next to the wave

## Slide 35
Only one neighbor diagonally

## Slide 36
Therefore 6+3 = 9

## Slide 38
5+3 = 8

## Slide 39
Full wave

## Slide 40
New wave

## Slide 46
The wave reaches the robot

## Slide 47
There exists a path between the starting point and the destination

## Slide 48
The robot examines the neighbors

## Slide 49
Steps to the lowest one

## Slide 54
The destination is in its ambient

## Slide 55
Reached it

## Slide 56
With obstacle

## Slide 57
The propagation starts from the destination

## Slide 58
Same method like without obstacles

## Slide 70
The obstacle is passed

## Slide 71
Examine the neighbours

## Slide 74
The robot has been reached

## Slide 84
The destination is in the robot’s scope

## Slide 86
Comments
The methodology is algorithmic
Once more the operation:
1)We start to propagate from the destination
2) Searching for empty cells with wavefronts in the neighborhood
3) Checking the surrounding cells, searching for lowest cost
4) Identifying the value of the new cell (previous + cost of the step)
Repeating steps 2-4 until we reach the robot or we could expand further
Once we have reached the robot:
We find the cell with the lowest value and make a step towards it
We repeat the first point until we won’t reach the destination