## Slide 1
Dezső Sima
Intel’s Core 2 family
Overview
Sept. 2022
Vers. 3.3
© Dezső Sima 2022

## Slide 2: Introduction (1)
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smarphones
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smartphones
Up to 64 C
Up to 32 C
Up to 10 + G
GPU less: Up to (8 + 16) C + G
With iGPU: Up to (8 +16) C + G
Recent config.
Remark: Intel and AMD usually designate their laptop processors as mobile processors.
Recent major processor categories
Servers
Recent major processor categories
Clients
(Desktops/Laptops
HEDTs
(High-End Desktops)
Mobiles
(Tablets/Smartphones)

## Slide 3: Introduction (2)
The processor war: desktops/laptops
Image source: [43]

## Slide 4: Introduction (3)
AMD’s claims of leadership in GPU-less DTs (7 nm Ryzen 5000 line, 2020) [46]

## Slide 5: Introduction (4)
Gaming performance
GeForce RTX 3090 FE graphics card [44]
(average FPS)
With their Alder Lake line Intel regained leadership in the client market segment in 2021.
Intel’s response: the 12. gen. 10 nm big.little Alder Lake line (2021)

## Slide 6: Introduction (5)
Remark
Transistor densities (100 million transistors/mm2) of major wafer foundries [47]
This is the reason why Intel introduced a new renaming scheme of its IC
manufacturing processes (called also nodes) while depriving nm data, as follows:
This Figure shows that concerning transistor density e.g. Intel’s 10 nm technology
is roughly equivalent to TSMC’s (Taiwan Semiconductor Manufacturing Company)
7 nm technology or Intel’s 7 nm technology roughly equals TSMC’s 5 nm or Samsung’s 3 nm
technology.

## Slide 7: Introduction (6)
Intel’s new process naming scheme from 07/2021 []
TSMC
10 nm
TSMC
7 nm
TSMC
5 nm?
≈ TSMC
equivalence

## Slide 8: Introduction (7)
Intel’s astonishing process evolution roadmap revealed in 12/2019 [12]
EUV: Extreme ultraviolet lithography
(Alder Lake
Raptor Lake)
(Meteor Lake)

## Slide 9: Introduction (8)
AMD’s contra: Zen4-based Ryzen 7000 DTs on TSMC’s 5 nm technology (2022) [45 ]-1
Core i9-12900K: Alder Lake DT
Ryzen 9-7950X: Ryzen 9000 DT

## Slide 10: Introduction (9)
AMD’s contra: Zen4-based Ryzen 7000 DTs on TSMC’s 5 nm technology (2022) [45 ]-2

## Slide 11: Introduction (10)
What’s next from Intel?
Image source: AdoredTV
13. gen. 10 nm (“Intel 7” techn.)
Raptor Lake (8+16 cores)
To be launched: 10/2022
14. gen. 7 nm (“Intel 4?” techn.)
Meteor Lake
To be launched: 2023

## Slide 12: Introduction (11)
The processor war: mobiles
Apple’s A15/A14 vs. Qualcomm/Samsung/MediaTek Performance/energy consumption
[48]
S: Snapdragon (Qualcomm)
E: Exynos (Samsung)
D: Dimensity (MediaTek)
GS101 (Google)

## Slide 13: Introduction (12)
The processor war: servers
Intel Xeon vs. AMD EPYC vs. ARM-based servers (ARM Neoverse-based, Amper Altra)
per-thread performance [49]

## Slide 14
Intel’s Core 2 family - Overview
1. Overview of the evolution of Intel's Pentium 4 and
Core 2 families
2. Evolution of desktop and laptop processors
3. Evolution of HEDT (High-End Desktop) processors
4. Evolution of high-end 2S server processors
5. Evolution of tablet- and smartphone processors
Notes: 14

## Slide 15
1.1 Overview of the evolution of Intel's Pentium 4 family
Notes: 15

## Slide 16: 1.1 Overview of the evolution of Intel's Pentium 4 family (1)
At Pentium 4's launch (Nov. 2000) Intel's vice president (Otellini) claimed that the
lifespan of the Netburst microarchitecture, which is the foundation of the Pentium 4
family, would be 7 years and its expected clock frequency would break the 10 GHz
mark in 2006 [4].
1.1 Overview of the evolution of Intel's Pentium 4 family
Announcing and aims of Intel’s Netburst microarchitecture

## Slide 17: 1.1 Overview of the evolution of Intel's Pentium 4 family (2)
Key innovations of the Netburst microarchitecture and the Pentium 4 family
Beyond the new Netburst microarchitecture the Pentium 4 family introduced two
major innovations
hyperthreading (along with the 2. core (Northwood)) in 2002 and
64-bit architecture (along with the 3 core (Prescott)) in 2004,
as indicated in the next Figure.

## Slide 18: 1.1 Overview of the evolution of Intel's Pentium 4 family (3)
Key new features of the ISP
and the microarchitecture
New microarch., 64-bit
Dual cores (DC) for the
Pentium D (Smithfield) (05/2005)
01/2006
90nm
130nm
TICK TOCK
2 YEARS
2 YEARS
2 YEARS
65nm
TICK Pentium 4 (Cedar Mill SC)
Pentium D (Presler DC)
TOCK Core 2
2 YEARS
New microarch.
called Netburst
New microarch.,
Hyperthreading (HT)
Pentium 4 /Northwood
TICK TOCK
TICK TOCK
Pentium 4 /Prescott
Pentium 4 /Willamette
07/2006
11/2000
01/2002
02/2004
180nm
Overview of the evolution of Intel's Pentium 4 and Core 2 families (Based on [5])
The Pentium 4 family includes 3 generations and introduced important innovations,
as listed below.
Note
This is a single phase development model, in each generation both technology and
microarchitecture had been changed.
Dual cores were implemented as dual dies enclosed into the same socket.

## Slide 19: 1.1 Overview of the evolution of Intel's Pentium 4 family (4)
Relative dissipation of Intel's x86 family of processors
Pentium 4
Pentium III
Pentium
≈ Limit of air cooling

## Slide 20: 1.1 Overview of the evolution of Intel's Pentium 4 family (5)
Rising the dissipation (D) per cm2 die area [W/cm2] in Intel's Pentium family -2
As the previous Figure shows, the dissipation of Pentium 4’s subsequent cores
dynamically rose, up to nearly 100 W/cm2 for the 3. core (Prescott) that equals
about 100 W, as it has a die area of approximately 1 cm2.
But this steep rise of dissipation could not be kept on further on while the
resulting power density became unmanageable high, since absorbing about 100 W
dissipation by means of air cooling was already a challenge in DTs of that time.
As a consequence, due to overheating Intel could not achieve the announced
4 GHz clock frequency.

## Slide 21: 1.1 Overview of the evolution of Intel's Pentium 4 family (6)
Figure: In Oct. 2004 Crag Barrett, Intel's then-CEO on his knees to apologize for
not achieving the 4GHz mark in front of an audience of 7000 informatics professional
at the IT Expo in Orlando [6]
Announcing Intel’s incapability to achieve 4 GHz in their Pentium 4 line
In Oct. 2004 Intel's CEO (Chief Executing Officer) admitted that the Pentium 4
family would not achieve 4 GHz [6].

## Slide 22: 1.1 Overview of the evolution of Intel's Pentium 4 family (7)
Cancellation of the Pentium 4 line due to overheating
Basically due to overheating the Pentium 4 line could not achieve their targets so
it was withdrawn in 2005.

## Slide 23: 1.1 Overview of the evolution of Intel's Pentium 4 family (8)
Intel's Pentium 4 family
180 nm
130 nm
90 nm

## Slide 24
Switching Intel's processor design paradigm to cope with raising dissipation about 2003
Figure 1.3: Intel’s plan to develop their manufacturing technology and processor lines
revealed at a shareholder’s meeting back in 4/2006 [7]
1.1 Overview of the evolution of Intel's Pentium 4 family (9)
Allready in 2003 Intel became aware of the overheating problem and shifted the focus
of their processor development from the pure performance goal to the aspect of
performance per watt, as stated in a slide from 4/2006, see below.

## Slide 25
With the advent of mobile devices (about 2006) a new design paradigm arose as well,
as mobile devices require long operating hours i.e. low power consumption,
in sharp contrast to the design paradigm of traditional processors, as indicated below.
1.1 Overview of the evolution of Intel's Pentium 4 family (10)
Remark: A further change of the design paradigm for designing the mobile processors
High performance/power
(e.g. GFLOPS/Watt)
Traditional processors
Tablets and smartphones
Low power
(Watt)
(Number of operating hours)

## Slide 26: 1.1 Overview of the evolution of Intel's Pentium 4 family (11)
Falling back to a low-power design for the next (Core 2) family
Furthermore, as dissipation was the major cause for cancelling the Pentium 4 family,
in planning the subsequent Core 2 family, Intel fell back to a low power mobile design,
which is the Pentium M line.

## Slide 27: 1.1 Overview of the evolution of Intel's Pentium 4 family (12)
Announcing and aims of Intel’s Netburst microarchitecture
Key innovations of the Netburst microarchitecture and the Pentium 4 family
Summing up key issues of the evolution of Intel’s Pentium 4 family -1
At Pentium 4's launch (Nov. 2000) Intel's vice president (Otellini) claimed that the
lifespan of the Netburst microarchitecture, the foundation of the Pentium 4 family,
would be 7 years and its expected clock frequency would break the 10 GHz mark
in 2006 [4].
Beyond the new Netburst microarchitecture the Pentium 4 family introduced two
major innovations
hyperthreading (along with the 2. core (Northwood) in 2002 and
64-bitarchitecture (along with the 3 core (Prescott) in 2004.
Note that the Pentium 4 line is designed on a single phase development model,
in each generation both technology and microarchitecture had been changed.

## Slide 28: 1.1 Overview of the evolution of Intel's Pentium 4 family (13)
Cancellation of the Pentium 4 line due to overheating
Switching Intel's processor design paradigm to cope with raising dissipation about 2003
Rising of dissipation (D) per cm2 die area [W/cm2] in Intel's Pentium family -2
The dissipation of Pentium 4’s subsequent cores dynamically rose, up to nearly
100 W/cm2 for the 3. core (Prescott) that equals about 100 W, as it has a die area
of approximately 1 cm2.
But this steep rise of dissipation could not be kept on further on while the
resulting power density became unmanageable high, since absorbing about 100 W
dissipation by means of air cooling was already a challenge in DTs of that time.
As a consequence, due to overheating Intel could not achieve the announced
4 GHz clock frequency.
Summing up key issues of the evolution of Intel’s Pentium 4 family -2
Already in 2003 Intel became aware of the overheating problem and shifted the focus
of their processor development from the pure performance goal to the aspect of
performance per watt, as stated in a slide from 4/2006, see below.
Cancellation of the Pentium 4 line due to overheating
Basically due to overheating the Pentium 4 line could not achieve their targets so
it was withdrawn in 2005.

## Slide 29: 1.1 Overview of the evolution of Intel's Pentium 4 family (14)
Falling back to a low-power design for the next (Core 2) family
Summing up key issues of the evolution of Intel’s Pentium 4 family -3
Furthermore, as dissipation was the major cause for cancelling the Pentium 4 family,
in planning the subsequent Core 2 family Intel fell back to a low power mobile design,
that is the Pentium M line.

## Slide 30
1.2 Overview of the evolution of Intel's Core 2 family
Notes: 30

## Slide 31: 1.2 Overview of the evolution of Intel's Core 2 family (1)
1.2 Overview of the evolution of Intel's Core 2 family
Introduction
Since about 2006 for more than 10 years Intel’s Core 2-based processors lead the
performance race and dominated the client and server processor lines.
Nevertheless, in the last couple of years they face a fierce competition by AMD’s
Zen-based DT and server processors and also by ARM ISA-based servers
(from Ampere and AWS).

## Slide 32: 1.2 Overview of the evolution of Intel's Core 2 family (2)
Intel’s two-phase processor development model
First, Core 2 processor generations appeared in two year cycles, according to a
two-phase Tick-Tock model such that
in the Tick phase Intel basically reduced the feature size by about 0.7
whereas
in the Tock phase enhanced the microarchitecture,
as the next Figure will indicate it.

## Slide 33: 1.2 Overview of the evolution of Intel's Core 2 family (3)
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
(2006)
(2007)
(2008)
(2010)
(2011)
(2012)
(2013)
(2014)
Two phase processor development in the 1-5 generations of the Core 2 family -1

## Slide 34: 1.2 Overview of the evolution of Intel's Core 2 family (3b)
Note that a feature size reduction of 0.7 allows to implement the same number
of transistors on ~ ½ Si die area or
to double the transistor count on the same Si area.
The aim of the two-phase approach was to reduce the huge complexity of the
development process for better manageability.
Two phase processor development in the 1-5 generations of the Core 2 family -2

## Slide 35: 1.2 Overview of the evolution of Intel's Core 2 family (4)
Two phase processor development in the 1-5 generations of the Core 2 family -3
The two year evolution cycle coincided with Moore’s law as long as Intel reduced the
feature size from 65 nm to 14 nm, but the cadence of the evolution became soon
lengthened when Intel encountered manufacturing difficulties to master the 10 nm
process, as indicated in the next Figure.
Remark
Originally, Intel planned the 10 nm technology to introduce already in 2015, as the
firm’s 2011 technology roadmap from 2011 indicates [42].
In fact, Intel 10 nm process became only available in 2018 (as a pilot implementation)
and in 2019 as an available technology for mass production.

## Slide 36: 1.2 Overview of the evolution of Intel's Core 2 family (5)
The last two technology transitions have signaled that our cadence today is closer
to 2.5 years than two“ [8].
In fact, the cadence of Intel’s IC development process almost doubled.
On Intel’s Q2 2015 earnings conference call, on July 16 2015, Krzanich, Intel's CEO
(Chief Executive Officer) told: “in the second half of 2017, we expect to launch our
first 10-nanometer product, code named Cannon Lake.
Lengthening the cadence of Intel’s IC development to
2000
2002
2004
2006
2008
2010
2012
2014
2016
2018
200
180
160
140
120
100
80
60
40
0
20
180 nm
130 nm
90 nm
65 nm
45 nm
32 nm
22 nm
14 nm
10 nm
Pentium 4
Northwood
Pentium 4
Prescott
Pentium 4
Cedar Mill
Penryn
Westmere
Ivy Bridge
Broadwell
Pentium 4
Willamette
Cannon Lake
01/02
02/04
11/07
01/10
04/12
09/14
11/00
05/18
01/06
nm
≈ 3.5 years

## Slide 37: 1.2 Overview of the evolution of Intel's Core 2 family (6)
Replacing the two cycle Tick-Tock development model by a three-phase
model including one or more optimization cycles [9]
Figure: Intel’s switch to a three-phase development model [10]
After having encountered difficulties in switching to the 10 nm process Intel
announced a 3-phase development model, including a Modification phase as well,
as seen below.

## Slide 38: 1.2 Overview of the evolution of Intel's Core 2 family (7)
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TICK
TOCK
TICK
TOCK
TICK
TOCK
gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
(2006)
(2007)
(2008)
(2010)
(2011)
(2012)
(2013)
(2014)
Optimization cycles introduced in Intel’s processor development model
1. Introduction (1)
(2015)
(2016)
(2017/18)
Skylake
New
Microarch.
14 nm
TOCK
Optimization
6. gen.
Optimization
7. gen.
8. gen.1
Kaby Lake
New
Microarch.
14 nm
Kaby Lake R/G
Coffee Lake
Amber Lake-Y
Whiskey Lake-U
Cannon Lake (10 nm)
14 nm
Coffee Lake R
New
Microarch.
14 nm
Optimization
9. gen.
(2018)
R: Refresh
Kaby Lake Refresh
Kaby Lake G with AMD Vega
graphics
Coffee Lake
Amber Lake Y
Whiskey Lake U
(all 14 nm) and
Cannon Lake (10 nm)
1The 8th generation encompasses
the following processor lines:
Comet Lake
New
Microarch.
14 nm
Optimization
10. gen.
(2019)
lines [11].

## Slide 39: 1.2 Overview of the evolution of Intel's Core 2 family (8)
Note that the 8th generation covers a number of new families with more or less
enhancements manufactured still on the 14 nm process.
In addition, as part of the 8th Intel introduced the 10 nm Cannon Lake line
(merely a dual core GPU-less low-power processor) in 05/2018 to demonstrate
its 10 nm process capability.
At this time however, Intel did not yet possessed a refined process needed for
mass producing 10 nm dies.
Remarks to the 8th generation

## Slide 40: 1.2 Overview of the evolution of Intel's Core 2 family (9)
Optimization cycles introduced after the 10th Ice Lake generation
Tiger
Lake
New
Microarch.
10 nm
Alder Lake
New Hybrid
Microarch.
10 nm
Optimization
New design
11. gen.
12. gen.
(2020)
(2021)
Ice
Lake
New
Microarch.
10 nm
TOCK
10. gen.
(2019)
Cannon
Lake
New
Process
10 nm
TICK
8. gen.
(2018)
Rocket Lake
New hybrid
Microarch.
14 nm
Back porting
11. gen.
(2021)
Remarks
Intel’s first mass-produced 10 nm processors were the 10th gen. Ice Lake processors.
Next Intel introduced the optimized 11th gen. Tiger Lake line and subsequently also
the 11th gen. Rocket Lake line, which is a 14 nm backporting of the 10 nm 10th gen.
Ice Lake core with additional enhancements, not detailed here.
Raptor Lake
New Hybrid
Microarch.
10 nm
Optimization
13. gen.
(2022)

## Slide 41: 1.2 Overview of the evolution of Intel's Core 2 family (10)
Introducing hybrid (big.little) microarchitectures
The 12th gen. Alder Lake family (2021) has a new, hybrid design incorporating
high-performance (P) an high-efficiency (E) cores.
Tiger
Lake
New
Microarch.
10 nm
Alder Lake
New Hybrid
Microarch.
10 nm
Optimization
New design
11. gen.
12. gen.
(2020)
(2021)
Ice
Lake
New
Microarch.
10 nm
TOCK
10. gen.
(2019)
Cannon
Lake
New
Process
10 nm
TICK
8. gen.
(2018)
Rocket Lake
New hybrid
Microarch.
14 nm
Back porting
11. gen.
(2021)
Figure: Intel’s
12th gen. Alder Lake line
It will cover all processor segments from mobiles to servers.
In fact, it is not Intel’s first hybrid design, since Intel introduced already one year
earlier the mobile oriented multi-die Lakefield family with big.little CPU cores,
but the firm didn’t enroll it into the sequence of processor generations.
Intel designates the 10 nm manufacturing process of the Alder Lake processors
as the Intel 7 process, as discussed earlier.

## Slide 42
Basic architectures | Basic architectures and their shrinks
Pentium 4 (Prescott) | 2005 90 nm Pentium 4 2006 65 nm Pentium 4
Core 2 | 2006 65 nm Core 2 2007 45 nm Penryn
Nehalem | 2008 45 nm Nehalem 2010 32 nm Westmere
Sandy Bridge | 2011 32 nm Sandy Bridge 2012 22 nm Ivy Bridge
Haswell | 2013 22 nm Haswell 2014 14 nm Broadwell
Skylake | 2015 14 nm Skylake 14 nm Kaby Lake 14 nm Coffee Lake 10 nm Cannon Lake
Icelake | 2019 10 nm Icelake
1.2 Overview of the evolution of Intel's Core 2 family (11)
Basic microarchitectures and their related shrinks
Presented from Pentium 4’s 3rd core (Prescott) until the 10th gen. Icelake.

## Slide 43: 1.2 Overview of the evolution of Intel's Core 2 family (12)
Presentation at AMD's Financial Analyst Day May 16 2017
Flattening the rise of clock frequencies while transistor technology evolved [13]

## Slide 44: 1.2 Overview of the evolution of Intel's Core 2 family (13)
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
Haifa
Oregon
Oregon
Oregon
Haifa
Haifa
Oregon
Oregon
Two competing design centers -1
1. Introduction (1)
Skylake
New
Microarch.
14 nm
TOCK
TOCK
6. gen.
TOCK
7. gen.
8. gen.1
Kaby Lake
New
Microarch.
14 nm
Kaby Lake R/G
Coffee Lake
Amber Lake-Y
Whiskey Lake-U
(Cannon Lake 10 nm)
14 nm
Coffee Lake R
New
Microarch.
14 nm
TOCK
9. gen.
R: Refresh
Kaby Lake Refresh
Kaby Lake G with AMD Vega
graphics
Coffee Lake
Amber Lake Y
Whiskey Lake U
(all 14 nm) and
Cannon Lake (10 nm)
1The 8th generation encompasses
the following processor lines:
Comet Lake
New
Microarch.
14 nm
TOCK
10. gen.
lines [11].
Haifa
Haifa
Haifa
Haifa
Haifa

## Slide 45: 1.2 Overview of the evolution of Intel's Core 2 family (14)
Two competing design centers -2
Tiger
Lake
New
Microarch.
10 nm
Alder Lake
New Hybrid
Microarch.
10 nm
Optimization
New design
11. gen.
12. gen.
Ice
Lake
New
Microarch.
10 nm
TOCK
10. gen.
Cannon
Lake
New
Process
10 nm
TICK
8. gen.
Rocket Lake
New hybrid
Microarch.
14 nm
Back porting
11. gen.
Haifa
Haifa
Haifa
Haifa
Haifa
Raptor Lake
New Hybrid
Microarch.
10 nm
Optimization
13. gen.
Haifa?

## Slide 46: 1.2 Overview of the evolution of Intel's Core 2 family (15)
Naming scheme of Core 2 lines -1
Intel introduced a more or less standard naming scheme for their Core 2 family along
with the 2nd gen. Sandy bridge processors that differs in client, HEDT and server lines.
Client processor names are typically composed of
the i3/i5/i7/i9 brand modifier followed by a hyphen,
a four digit model number with the first digit indicating the generation
and the next three digits supplementing it and
a product line suffix, mostly referring to the TDP value of the processor,
as seen below for the 7th gen. i7-7500U Kaby Lake DT processor with a
TDP of 15 W.
Figure: Naming scheme of client processors in Intel’s Core family [14]

## Slide 47: 1.2 Overview of the evolution of Intel's Core 2 family (16)
Remark: Most frequently used suffixes and related TDP values in Intel’s client lines
Y: ultra low-power (11.5/13 W, SoC), when regular naming (i3/i5/i7-nxxxY) is used
or extreme low power (4.5/5 W SoC, when irregular naming m3/m5/m7-nYxx) is used
U: low power (typically 15/28 W, SoC)
H: high-performance mobile (typically 35/45 W)
Mobile suffixes
Desktop suffixes
T – power-optimized models (ultra low power with 35/45 W TDP)
S – performance-optimized models (low power with 65 W TDP)
K – unlocked (adjustable CPU multiplier (60-95 W)
SoC: System on a Chip (egylapkás rendszer)

## Slide 48: 1.2 Overview of the evolution of Intel's Core 2 family (17)
Naming scheme of Core 2 lines -2
HEDT processor names are typically composed of
the i7/i9 brand modifier followed by a hyphen and
a four digit model number with the first digit indicating the
generation identifier plus one, then the digit 8 or 9 along with a 2-digit
model specifier, and
usually the E, EE or X tag,
like i9-7900X for a 6th gen. Skylake HEDT processor

## Slide 49: 1.2 Overview of the evolution of Intel's Core 2 family (18)
Server processor names (from Sandy Bridge up to the Broadwell family) are composed of
the E3/E5/E7 product line identifier (for Enterprise) followed by a hyphen,
a four digit model number with the first digit indicating the max. number
of sockets the server may support (1, 2 4 or 8),
a further digit (Socket type) identifying the targeted market segment (4 for entry
level (EN), 6 for effective performance (EP) or 8 for extreme performance (EX),
two digits for the model number and
a version identifier (without any version number for Westmere/Sandy Bridge,
v2 for Ivy Bridge, v3 for Haswell etc,
as seen below for the 5th gen. Broadwell-based extreme performance (EX)
E7-4820v4 server processor supporting up to 4 sockets.
Figure: Intel’s naming scheme for server processors up to the Broadwell family [15]
Naming scheme of Core 2 lines -3
From the Skylake server line on Intel changed its naming scheme (not discussed here).
(Brand
modifier)

## Slide 50: 1.2 Overview of the evolution of Intel's Core 2 family (19)
Naming of Intel’s Core 2 processors at a glance -1
1. Introduction (1)
EE
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
gen.
4/5/6xxx
2. gen.
2xxx
3. gen.
3xxx
4. gen.
4xxx
5. gen.
5xxx
Broad-
well
New
Process
14 nm
TICK
HEDTs
Servers
38/39xx
E3/E5/E7-xxxx
48/49xx
v2
58/59xx
v3
68/69xx
v4
i5/i7-xxx
980/990
E7-xxx
i7-965/975
3/5xxx
i3/i5/i7-xxx
Clients
QX 96/97xx
3/5/7xxx
X/QX 6xxx
3/5/7xxx
6/7/8/9xxx
Skylake
New
Microarch.
14 nm
TOCK
TOCK
6. gen.
6xxx
TOCK
7. gen.
7xxx
8. gen.1
i9 8xxx
Kaby Lake
New
Microarch.
14 nm
Kaby Lake R/G
Coffee Lake
Amber Lake-Y
Whiskey Lake-U
14 nm
Coffee Lake R
New
Microarch.
14 nm
TOCK
9. gen.
9xxx
R: Refresh
Kaby Lake Refresh
Kaby Lake G with
AMD Vega graphics
Coffee Lake
Amber Lake Y
Whiskey Lake U
(all 14 nm) and
Cannon Lake (10 nm)
1The 8th generation
encompasses the following
processor lines:
Comet Lake
New
Microarch.
14 nm
TOCK
10. gen.
10xxx
lines [11].
i7-78xx/i9-79xx
i5-76xx/i7-77xx
© Dezső Sima 2020
Clients
14 nm

## Slide 51: 1.2 Overview of the evolution of Intel's Core 2 family (20)
Naming of Intel’s Core 2 processors at a glance -2
Tiger
Lake
New
Microarch.
10 nm
Alder Lake
New Hybrid
Microarch.
10 nm
Optimization
New design
11. gen.
12. gen.
(2020)
(2021)
Ice
Lake
New
Microarch.
10 nm
TOCK
10. gen.
(2019)
Cannon
Lake
New
Process
10 nm
TICK
8. gen.
(2018)
Rocket Lake
New hybrid
Microarch.
14 nm
Back porting
11. gen.
(2021)
i3-8121U
Clients
i5-i9-11xxx
i3/i5/i7-10xxx
i3-i9-12xxx
i3-i9-11xxx
14 nm
Raptor Lake
New Hybrid
Microarch.
10 nm
Optimization
13. gen.
(2022)
i5-i9-13xxx

## Slide 52: 1.2 Overview of the evolution of Intel's Core 2 family (21)
Key enhancements of the Core family (clients)
Key enhancements of the Core family
Key ISA extensions
SIMD extensions
Key enhancements of the microarchitecture
128-bit FX SSSE3
128-bit FX/FP SSE4
256-bit FP-AVX
256-bit FX/FP AVX2
512-bit FX/FP AVX512

## Slide 53: 1.2 Overview of the evolution of Intel's Core 2 family (22)
PII
Klamath,
(1997)
Pentium_MMX
(1997)
Core
Cannon-Lake,
(2018)
Skylake-X/SP,
(2017)
(2016)
Evolution of Intel’s
x86 ISA extensions [16]

## Slide 54: 1.2 Overview of the evolution of Intel's Core 2 family (23)
Key enhancements of the Core 2 microarchitecture to raise performance
Key enhancements
to raise performance
Key enhancements of the Core family
Key enhancements
in power management
(see next Figure)
Integrated memory controller
(NUMA architecture)
Integrated GPU
Private per-core L2 caches
with a shared L3 cache
Ring bus interconnect
Integrated PCIe controller
Raising the front-end width
of the cores (to 4/5/6)
Raising the back-end width
of the cores (from 5 to 17)
Raising the core count
(from 2 up to 16 in mobiles/DTs and
from 2 up to 56 in servers)
Key ISA extensions
SIMD extensions
(shown previously)
Key enhancements of the microarchitecture

## Slide 55: 1.2 Overview of the evolution of Intel's Core 2 family (24)
Key ISA and microarchitecture innovations of the Core 2 family (based on [5]) -1
Key new features of the ISA
and the microarchitecture
New microarch.: 4-wide core,
128-bit SIMD FX/FP EUs,
shared L2 , no HT
New microarch.: 256-bit (FP) AVX,
ring bus, integrated GPU
New microarch.: 256-bit (FX) AVX2,
L4 cache (discrete eDRAM), TSX
Shared Virtual Memory
In package integrated GPU
New microarch.: 4 cores, integr. MC,
QPI, private L2, (inclusive) L3, HT
New microarch.: 5-wide core,
ISP, Memory Side L4 cache, no FIVR
Optane memory, in KBL G series:
in package integr. CPU, GPU, HBM2
6C, (PCHs of S-series DTs support:
USB G2, integr. conn., Optane 2)
8C
2 YEARS
11/2007
01/2006
65nm
TICK Pentium 4 ( Cedar Mill)
Pentium D (Presler)
TOCK Core 2
07/2006
11/2008
01/2011
01/2010
32nm
45nm
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TOCK Haswell
04/2012
06/2013
09/2014
10/2015
14nm
6 YEARS
08/2016
08/2017
2 YEARS
10/2017
10/2018
TOCK Kaby Lake Refresh
TOCK Kaby Lake
TOCK Skylake
14nm
TICK Broadwell
TICK Ivy Bridge
2 YEARS
TOCK Coffee Lake Refresh
TOCK Coffee Lake
2G
3G
4G
5G
6G
7G
8G
8G
9G
1G
TOCK Comet Lake
10G
08/2019
TOCK Amber/Whiskey Lake
08/2018
8G
10C

## Slide 56: 1.2 Overview of the evolution of Intel's Core 2 family (25)
Key new features of the ISA
and the microarchitecture
New microarchitecture
Thunderbolt 3, WiFi 6
AVX 512
Key ISA and microarchitecture innovations of the Core 2 family (based on [5]) -2
05/2018
07/2019
10nm
4 YEARS
TICK Cannon Lake
TOCK Ice Lake
TOCK Alder Lake
TOCK Tiger Lake
09/2020
11/2021
11G
12G
10G
8G
New big-little microarchitecture,
8+8 cores, 6-wide P cores
8+16 cores
2 YEARS
TICK Pentium 4 ( Cedar Mill)
Pentium D (Presler)
TOCK Core 2
Backporting to 14 nm
Rocket Lake
11G
14nm
03/2021
13G
10/2022?
TOCK Raptor Lake

## Slide 57: 1.2 Overview of the evolution of Intel's Core 2 family (26)
Intel’s IPC improvements achieved from the Pentium M (Dothan) to the Ice Lake [17] -1
The reference processor is Intel’s Pentium M processor (codename Dothan) (2003)
(Core 2
(2006))
(Pentium M
(2004))

## Slide 58: 1.2 Overview of the evolution of Intel's Core 2 family (27)
Intel’s IPC improvements achieved from the Pentium M (Dothan) to the Ice Lake [17] -1
As the preceding Figure indicates Intel achieved a nearly twofold IPC increase
in their Core 2 family up to the Ice Lake line.

## Slide 59: 1.2 Overview of the evolution of Intel's Core 2 family (28)
Key enhancements
to reduce power consumption
Power gating
PCU (Power Control Unit)
FIVR) Fully Integrated Voltage Regulator)
Speed Shift Technology (CPPC)
Hybrid (big.little architecture)
Key enhancements to raise performance if there is a power/temperature headroom
Turbo Boost technology
Turbo Boost 2.0
Turbo Boost 3.0
Key enhancements in power management
Key enhancements of the microarchitecture in power management

## Slide 60: 1.2 Overview of the evolution of Intel's Core 2 family (29)
Key power management innovations of the Core 2 family (based on [5]) -1
2 YEARS
11/2007
01/2006
65nm
TICK Pentium 4 ( Cedar Mill)
Pentium D (Presler)
TOCK Core 2
07/2006
11/2008
01/2011
01/2010
32nm
45nm
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TOCK Haswell
04/2012
06/2013
09/2014
10/2015
14nm
6 YEARS
08/2016
08/2017
2 YEARS
10/2017
10/2018
TOCK Kaby Lake Refresh
TOCK Kaby Lake
TOCK Skylake
14nm
TICK Broadwell
TICK Ivy Bridge
2 YEARS
TOCK Coffee Lake Refresh
TOCK Coffee Lake
2G
3G
4G
5G
6G
7G
8G
8G
9G
1G
TOCK Comet Lake
10G
08/2019
TOCK Amber/Whiskey Lake
08/2018
Key new features
of the power management
EDAT
Integrated Power Gates, PCU,
Turbo Boost
Turbo Boost 2.0
FIVR
2. gen. FIVR
Speed Shift Technology,
Duty Cycle control, No FIVR
except Skylake X
Speed Shift Technology v2
In H-series: TVB
(Thermal Velocity Boost)
STIM
Clock gating, PECI,
Platform Thermal Control by
3. party controller
8G

## Slide 61: 1.2 Overview of the evolution of Intel's Core 2 family (30)
Key new features
of the power management
FIVR, Dynamic Tuning 2.0
(not discussed)
Key power management innovations of the Core 2 family (based on [5]) -2
05/2018
07/2019
10nm
4 YEARS
TICK Cannon Lake
TOCK Ice Lake
TOCK Alder Lake
TOCK Tiger Lake
09/2020
11/2021
11G
12G
10G
8G
13G
10/2022?
TOCK Raptor Lake

## Slide 62: 1.2 Overview of the evolution of Intel's Core 2 family (31)
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smarphones
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smartphones
Up to 2x28 C
Up to 18 C
(Up to 10 C + G)
Up to 8 + 16 C + G
Recent config.
Remark: Intel usually designates its laptop processors as mobile processors.
Recent major processor categories and Intel’s related lines
Servers
Recent major processor categories and Intel’s related lines
Atom lines
Xeon E7/E5/E3
Platinum/Gold etc.
Clients
(Desktops/Laptops
Core i9/i7/i5/i3
(Basic architectures)
Atom lines
(+ LP Core models)
HEDTs
(High-End Desktops)
Core i7/i9
(Extreme Edition
or X models)
C a n c e l l e d i n 2 0 1 6
Mobiles
(Tablets/Smartphones)

## Slide 63: 1.2 Overview of the evolution of Intel's Core 2 family (32)
Example die sizes of Intel’s 14 nm processors (relative on scale) [18], [19]
Client dies
5th gen. Broadwell (2C, 82 mm2)
(with 5500 GPU)
Server die
6th gen. Skylake-SP (28C, ~680 mm2)
5th gen. Broadwell (2C, 133 mm2)
(with 6100/6200 GPU)

## Slide 64: 1.2 Overview of the evolution of Intel's Core 2 family (33)
Intel’s two-phase processor development model
Summing up key issues of the evolution of Core 2-based client processors -1
First, Core 2 processor generations appeared in two year cycles, according to a
two-phase Tick-Tock model such that
in the Tick phase Intel basically reduced the feature size by about 0.7 whereas
in the Tock phase enhanced the microarchitecture.
Note that a feature size reduction of 0.7 allows to implement the same number
of transistors on ~ ½ Si die area or
to double the transistor count on the same Si area.
or
The two year evolution cycle coincided with Moore’s law as long as Intel reduced
the feature size from 65 nm to 14 nm, but the cadence of the evolution became
soon lengthened when Intel encountered manufacturing difficulties to master
the 10 nm process.
After having encountered difficulties in switching to the 10 nm process Intel
announced a 3-phase development model, including a Modification phase as well.
Since about 2006 for more than 10 years Intel’s Core 2-based processors lead the
performance race and dominated the client and server processor lines.
Nevertheless, in the last couple of years they face a fierce competition by AMD’s
Zen-based DT and server processors and also by ARM ISA-based servers
(from Ampere and AWS).

## Slide 65: 1.2 Overview of the evolution of Intel's Core 2 family (34)
Introducing hybrid (big.little) microarchitectures
Summing up key issues of the evolution of Core 2-based client processors -2
The 12th gen. Alder Lake family (2021) has a new, hybrid design incorporating
high-performance (P) an high-efficiency (E) cores.
It will cover all processor segments from mobiles to servers.
In fact, it is not Intel’s first hybrid design, since Intel introduced already one year
earlier the mobile oriented multi-die Lakefield family with big.little CPU cores,
but the firm didn’t enroll it into the sequence of processor generations.
Key enhancements
to raise performance
(see subsequently)
Key enhancements of the Core family
Key enhancements
in power management
(see subsequently)
Key ISA extensions
SIMD extensions
Key enhancements of the microarchitecture
128-bit SIMD extensions
(SSE3-SSE4.1)
256-bit FP-AVX
256-bit FX/FP AVX2
512-bit FX/FP AVX512

## Slide 66: 1.2 Overview of the evolution of Intel's Core 2 family (35)
Summing up key issues of the evolution of Core 2-based client processors -3
Key enhancements
to raise performance
Key enhancements of the Core family
Key enhancements
in power management
(see next Figure)
Integrated memory controller
(NUMA architecture)
Integrated GPU
Private per-core L2 caches
with a shared L3 cache
Ring bus interconnect
Integrated PCIe controller
Raising the front-end width
of the cores (to 4/5/6)
Raising the back-end width
of the cores (from 5 to 17)
Raising the core count
(from 2 up to 16 in mobiles/DTs and
from 2 up to 56 in servers)
Key ISA extensions
SIMD extensions
(shown previously)
Key enhancements of the microarchitecture

## Slide 67: 1.2 Overview of the evolution of Intel's Core 2 family (36)
Summing up key issues of the evolution of Core 2-based client processors -4
C a n c e l l e d i n 2 0 1 6
Intel’s IPC improvements achieved from the Pentium M (Dothan) to the Ice Lake
All in all, Intel achieved a nearly twofold IPC increase in their Core 2 family up to
the Ice Lake line.
Key enhancements
to reduce power consumption
Power gating
PCU (Power Control Unit)
FIVR (Fully Integrated Voltage Regulator)
Speed Shift Technology (CPPC)
Hybrid (big.little architecture)
Key enhancements to raise performance if there is a power/temperature headroom
Turbo Boost technology
Turbo Boost 2.0
Turbo Boost 3.0
Key enhancements in power management
Servers
Recent major processor categories and Intel’s related lines
Atom lines
Xeon E7/E5/E3
Platinum/Gold etc.
Clients
(Desktops/Laptops
Core i7/i5/i3
(Basic architectures)
Atom lines
(+ LP Core models)
HEDTs
(High-End Desktops)
Core i7/i9
(Extreme Edition
or X models)
Mobiles
(Tablets/Smartphones)

## Slide 68
2. Evolution of client processors
2.1 Overview of Intel’s Core 2-based client processors
2.2 Evolution of core counts and memory support in Intel’s
Core 2-based client line
2.3 Evolution of key features of integrated graphics
in Intel’s Core 2 line
Notes: 68

## Slide 69: 2. Evolution of client processors (1)
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smarphones
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smartphones
Desktops
Servers
Recent major processor categories of Intel
Xeon E7/E5/E3
Platinum/Gold etc.
Clients
(Desktops/Laptops)
Core i9/i7/i5/i3
(Basic architectures)
HEDTs
(High-End Desktops)
Core i7/i9
(Extreme Edition
or X models)
2. Evolution of client processors
Mobiles
(Tablets/Smartphones)
Atom lines
Atom lines
(+ LP Core models)

## Slide 70
2.1 Overview of Intel’s Core 2-based client processors
Notes: 70

## Slide 71
2.1 Overview of Intel’s Core 2-based client processors -1
2.1 Overview of Intel’s Core 2-based client processors (1)
Gen. | Seg-ment | Attaching memory | Processor | Techno- logy | Max core count | Date of intro. | Socket | MCH/PCH | Mem. speed (up to) | Mem. channels
1. | M D | Attaching memory to the NB | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
 | D |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series | DDR3-1067 | 
 | D |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series | DDR3-1067 | 
 | D | Attaching memory to the processor die | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series | DDR3-1333 | 
 | M D |  | Westmere (M: Arrandale) D: Clarkdale/ | 32 nm | 2C+G | 1/2010 | M:BGA 1288 D:LGA 1156 | 5 Series |  | 
2. | M D |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | M: PGA 988 D: LGA 1155 | 6 series | DDR3-1333 | 
3. | M D |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 |  | 7 series | DDR3-1600 | 
4. | M D |  | Haswell | 22 nm | 4C+G | 6/2013 | M: BGA 1168 D: LGA 1150 | 8 Series | DDR3-1600 | 
4. | D |  | Haswell Refr. | 22 nm | 4C+G | 5/2014 |  | 9 Series | DDR3-1666 | 
5. | M D |  | Broadwell | 14 nm | 4C+G | 6/2015 |  | 9 Series | DDR3-1866 | 
 |  |  | Skylake | 14 nm | 4C+G | 10/2015 | M: BGA 1356 D: LGA 1151 | Series | DDR4-2133 | 
6. | M D |  |  |  |  |  |  |  |  | 
7. | M D |  | Kaby Lake | 14 nm | 4C + G | 8/2016 |  | 200 Series | DDR4-2400 | 
8. | M D |  | Coffee Lake | 14 nm | 6C +G | 10/2017 | M: BGA 1440 D: LGA 1151 | 300 Series | DDR4-2666 | 
8. | M |  | Amber Lake | 14 nm | 2C+G | 8/2018 | BGA 1515 | 300 Series | LPDDR3-2133 | 
8. | M |  | Whiskey Lake | 14 nm | 4C+G | 8/2018 | BGA 1528 | 300 Series | DDR4-2400 | 
9. | D |  |  |  |  |  |  |  |  | 
 |  |  | Coffee Lake R. | 14 nm | 8C +G | 10/2018 | LGA 1151 | 300 Series | DDR4-2666 | 
 |  |  | Comet Lake | 14 nm | 10C +G | 8/2019 | BGA 1528 LGA 1200 | 400 Series | DDR4-2666 | 
10. | M D |  |  |  |  |  |  |  |  | 
11. | D |  | Rocket Lake | 14 nm | 8C +G | 3/2021 | LGA 1200 | 400 Series | DDR4-3200 | 

## Slide 72
2.1 Overview of Intel’s Core 2-based client processors (2)
Gen. | Seg-ment | Attaching memory | Processor | Techno- logy | Max. core count | Date of intro. | Socket | PCH | Mem. speed (up to) | Mem. channels
8. | M | Attaching memory to the processor die | Cannon Lake | 10 nm | 2C | 5/2018 | BGA | n.a. | DDR4-2400 | 2
10. | M |  | Ice Lake | 10 nm | 4C+G | 7/2019 | Y: BGA 1377 U: BGA 1526 | 300-series | DDR4-3733 | 
11. | M D |  | Tiger Lake | 10 nm | 8C+G | 09/2020 | UP3: BGA 1449 UP4: BGA 1598 B/H: BGA 1787 | 400-series | LPDDR4x-4267 LPDDR5x-5400 | 
12. | M D |  | Alder Lake | 10 nm (Intel 7) | 8+8C+G | 11/2021 | M: BGA 1744 D: LGA 1700 | 600-series | DDR5-4800 | 4x 32-bit
13 | M D |  | Raptor Lake | 10 nm (Intel 7) | 8+16C+G | 09/2022 | LGA 1700 | 700-series | DDR5-5600 | 
Overview of Intel’s Core 2-based client processors -2
Remark
M: Mobile
D: Desktop
Note also that Intel’s mobile (actually laptop) oriented Core 2 processors typically have
BGA sockets whereas desktop processors LGA (in early lines PGA) sockets.
BGA: Ball Grid Array (forrasztó csúcsos tok)
LGA: Land Grid Array (érintkező tüs foglalat)
PGA: Pin Grid Array (érintkező tűs tok)

## Slide 73: 2.1 Overview of Intel’s Core 2-based client processors (3)
PGA
(Pin Grid Array)
LGA
(Land Grid Array)
BGA packages are soldered directly onto the motherboard, so practically they can not
be replaced without proper equipment.
PGA and LGA packages are inserted to their respective sockets.
Recent processor package types [169]
BGA
(Ball Grid Array)
LGA packages are essentially the direct opposite of PGAs, the contact pins are on the
socket, whereas contact pads on the package provide the connections.
In the PGA package pins provide the contacts, arranged in a regular array.
*

## Slide 74
2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line
Notes: 74

## Slide 75: 2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (1)
2.2 Evolution of core counts and memory support in Intel’s Core 2based client line
a) Evolution of core counts
Following the advances of the IC technology, maximum core counts of Intel’s
client processors rose already in 2007 from 2 to 4 and remained so roughly for 10 years,
as most earlier applications did not offer much more parallelism that might have
been utilized (see the next Figure).

## Slide 76
Raising max. core counts from 2 to 4 in Core 2-based client platforms -1
2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (2)
Gen. | Seg-ment | Attaching memory | Processor | Techno- logy | Max core count | Date of intro. | Socket | MCH/PCH | Mem. speed (up to) | Mem. channels
1. | M D | Attaching memory to the NB | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
 | D |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series | DDR3-1067 | 
 | D |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series | DDR3-1067 | 
 | D | Attaching memory to the processor die | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series | DDR3-1333 | 
 | M D |  | Westmere (M: Arrandale) D: Clarkdale/ | 32 nm | 2C+G | 1/2010 | M:BGA 1288 D:LGA 1156 | 5 Series |  | 
2. | M D |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | M: PGA 988 D: LGA 1155 | 6 series | DDR3-1333 | 
3. | M D |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 |  | 7 series | DDR3-1600 | 
4. | M D |  | Haswell | 22 nm | 4C+G | 6/2013 | M: BGA 1168 D: LGA 1150 | 8 Series | DDR3-1600 | 
4. | D |  | Haswell Refr. | 22 nm | 4C+G | 5/2014 |  | 9 Series | DDR3-1666 | 
5. | M D |  | Broadwell | 14 nm | 4C+G | 6/2015 |  | 9 Series | DDR3-1866 | 
 |  |  | Skylake | 14 nm | 4C+G | 10/2015 | M: BGA 1356 D: LGA 1151 | Series | DDR4-2133 | 
6. | M D |  |  |  |  |  |  |  |  | 
7. | M D |  | Kaby Lake | 14 nm | 4C + G | 8/2016 |  | 200 Series | DDR4-2400 | 
8. | M D |  | Coffee Lake | 14 nm | 6C +G | 10/2017 | M: BGA 1440 D: LGA 1151 | 300 Series | DDR4-2666 | 
8. | M |  | Amber Lake | 14 nm | 2C+G | 8/2018 | BGA 1515 | 300 Series | LPDDR3-2133 | 
8. | M |  | Whiskey Lake | 14 nm | 4C+G | 8/2018 | BGA 1528 | 300 Series | DDR4-2400 | 
9. | D |  |  |  |  |  |  |  |  | 
 |  |  | Coffee Lake R. | 14 nm | 8C +G | 10/2018 | LGA 1151 | 300 Series | DDR4-2666 | 
 |  |  | Comet Lake | 14 nm | 10C +G | 8/2019 | BGA 1528 LGA 1200 | 400 Series | DDR4-2666 | 
10. | M D |  |  |  |  |  |  |  |  | 
11. | D |  | Rocket Lake | 14 nm | 8C +G | 3/2021 | LGA 1200 | 400 Series | DDR4-3200 | 

## Slide 77: 2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (3)
Key features of the evolution of Core 2-based client line
a) Evolution of the core counts -2
This situation has however changed when AMD entered the market with 8-core
(GPU-less) Zen processors in 2017 followed by 16-core (GPU-less) DT processors
in 2020.
To encounter the competition Intel raised the core count of its client processors
first to 6 then to 8, subsequently to 10, and in 2022 even to 24 in their 13th gen.
Raptor Lake processor line, as the next Figures indicates.

## Slide 78
Raising max. core counts beyond 4 in Core 2-based client platforms -2
2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (4)
Gen. | Seg-ment | Attaching memory | Processor | Techno- logy | Max core count | Date of intro. | Socket | MCH/PCH | Mem. speed (up to) | Mem. channels
1. | M D | Attaching memory to the NB | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
 | D |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series | DDR3-1067 | 
 | D |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series | DDR3-1067 | 
 | D | Attaching memory to the processor die | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series | DDR3-1333 | 
 | M D |  | Westmere (M: Arrandale) D: Clarkdale/ | 32 nm | 2C+G | 1/2010 | M:BGA 1288 D:LGA 1156 | 5 Series |  | 
2. | M D |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | M: PGA 988 D: LGA 1155 | 6 series | DDR3-1333 | 
3. | M D |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 |  | 7 series | DDR3-1600 | 
4. | M D |  | Haswell | 22 nm | 4C+G | 6/2013 | M: BGA 1168 D: LGA 1150 | 8 Series | DDR3-1600 | 
4. | D |  | Haswell Refr. | 22 nm | 4C+G | 5/2014 |  | 9 Series | DDR3-1666 | 
5. | M D |  | Broadwell | 14 nm | 4C+G | 6/2015 |  | 9 Series | DDR3-1866 | 
 |  |  | Skylake | 14 nm | 4C+G | 10/2015 | M: BGA 1356 D: LGA 1151 | Series | DDR4-2133 | 
6. | M D |  |  |  |  |  |  |  |  | 
7. | M D |  | Kaby Lake | 14 nm | 4C + G | 8/2016 |  | 200 Series | DDR4-2400 | 
8. | M D |  | Coffee Lake | 14 nm | 6C +G | 10/2017 | M: BGA 1440 D: LGA 1151 | 300 Series | DDR4-2666 | 
8. | M |  | Amber Lake | 14 nm | 2C+G | 8/2018 | BGA 1515 | 300 Series | LPDDR3-2133 | 
8. | M |  | Whiskey Lake | 14 nm | 4C+G | 8/2018 | BGA 1528 | 300 Series | DDR4-2400 | 
9. | D |  |  |  |  |  |  |  |  | 
 |  |  | Coffee Lake R. | 14 nm | 8C +G | 10/2018 | LGA 1151 | 300 Series | DDR4-2666 | 
 |  |  | Comet Lake | 14 nm | 10C +G | 8/2019 | BGA 1528 LGA 1200 | 400 Series | DDR4-2666 | 
10. | M D |  |  |  |  |  |  |  |  | 
11. | D |  | Rocket Lake | 14 nm | 8C +G | 3/2021 | LGA 1200 | 400 Series | DDR4-3200 | 

## Slide 79: 2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (5)
Raising max. core count beyond 4 in Core 2-based client platforms -3
Gen.C | Seg-ment | Attaching memory | Processor | Techno- logy | Max. core count | Date of intro. | Socket | PCH | Mem. speed (up to) | Mem. channels
8. | M | Attaching memory to the processor die | Cannon Lake | 10 nm | 2C | 5/2018 | BGA | n.a. | DDR4-2400 | 2
10. | M |  | Ice Lake | 10 nm | 4C+G | 7/2019 | Y: BGA 1377 U: BGA 1526 | 300-series | DDR4-3733 | 
11. | M D |  | Tiger Lake | 10 nm | 8C+G | 09/2020 | UP3: BGA 1449 UP4: BGA 1598 B/H: BGA 1787 | 400-series | LPDDR4x-4267 LPDDR5x-5400 | 
12. | M D |  | Alder Lake | 10 nm (Intel 7) | 8C+8C+G | 11/2021 | M: BGA 1744 D: LGA 1700 | 600-series | DDR5-4800 | 4x 32-bit
13 | M D |  | Raptor Lake | 10 nm (Intel 7) | 8C+16C+G | 09/2022 | LGA 1700 | 700-series | DDR5-5600 | 

## Slide 80: 2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (6)
b) Evolution of memory support in Intel’s client processors
Despite rising core counts from 2 to 24 Intel remained by implementing dual memory
channels, as the next two Tables show.
The number of memory channels implemented -1

## Slide 81
2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (7)
The number of memory channels implemented -2
Gen. | Seg-ment | Attaching memory | Processor | Techno- logy | Max core count | Date of intro. | Socket | MCH/PCH | Mem. speed (up to) | Mem. channels
1. | M D | Attaching memory to the NB | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
 | D |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series | DDR3-1067 | 
 | D |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series | DDR3-1067 | 
 | D | Attaching memory to the processor die | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series | DDR3-1333 | 
 | M D |  | Westmere (M: Arrandale) D: Clarkdale/ | 32 nm | 2C+G | 1/2010 | M:BGA 1288 D:LGA 1156 | 5 Series |  | 
2. | M D |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | M: PGA 988 D: LGA 1155 | 6 series | DDR3-1333 | 
3. | M D |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 |  | 7 series | DDR3-1600 | 
4. | M D |  | Haswell | 22 nm | 4C+G | 6/2013 | M: BGA 1168 D: LGA 1150 | 8 Series | DDR3-1600 | 
4. | D |  | Haswell Refr. | 22 nm | 4C+G | 5/2014 |  | 9 Series | DDR3-1666 | 
5. | M D |  | Broadwell | 14 nm | 4C+G | 6/2015 |  | 9 Series | DDR3-1866 | 
 |  |  | Skylake | 14 nm | 4C+G | 10/2015 | M: BGA 1356 D: LGA 1151 | Series | DDR4-2133 | 
6. | M D |  |  |  |  |  |  |  |  | 
7. | M D |  | Kaby Lake | 14 nm | 4C + G | 8/2016 |  | 200 Series | DDR4-2400 | 
8. | M D |  | Coffee Lake | 14 nm | 6C +G | 10/2017 | M: BGA 1440 D: LGA 1151 | 300 Series | DDR4-2666 | 
8. | M |  | Amber Lake | 14 nm | 2C+G | 8/2018 | BGA 1515 | 300 Series | LPDDR3-2133 | 
8. | M |  | Whiskey Lake | 14 nm | 4C+G | 8/2018 | BGA 1528 | 300 Series | DDR4-2400 | 
9. | D |  |  |  |  |  |  |  |  | 
 |  |  | Coffee Lake R. | 14 nm | 8C +G | 10/2018 | LGA 1151 | 300 Series | DDR4-2666 | 
 |  |  | Comet Lake | 14 nm | 10C +G | 8/2019 | BGA 1528 LGA 1200 | 400 Series | DDR4-2666 | 
10. | M D |  |  |  |  |  |  |  |  | 
11. | D |  | Rocket Lake | 14 nm | 8C +G | 3/2021 | LGA 1200 | 400 Series | DDR4-3200 | 
*

## Slide 82: 2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (8)
The number of memory channels implemented -3
Gen. | Seg-ment | Attaching memory | Processor | Techno- logy | Max. core count | Date of intro. | Socket | PCH | Mem. speed (up to) | Mem. channels
8. | M | Attaching memory to the processor die | Cannon Lake | 10 nm | 2C | 5/2018 | BGA | n.a. | DDR4-2400 | 2
10. | M |  | Ice Lake | 10 nm | 4C+G | 7/2019 | Y: BGA 1377 U: BGA 1526 | 300-series | DDR4-3733 | 
11. | M D |  | Tiger Lake | 10 nm | 8C+G | 09/2020 | UP3: BGA 1449 UP4: BGA 1598 B/H: BGA 1787 | 400-series | LPDDR4x-4267 LPDDR5x-5400 | 
12. | M D |  | Alder Lake | 10 nm (Intel 7) | 8C+8C+G | 11/2021 | M: BGA 1744 D: LGA 1700 | 600-series | DDR5-4800 | 4x 32-bit
13 | M D |  | Raptor Lake | 10 nm (Intel 7) | 8C+16C+G | 09/2022 | LGA 1700 | 700-series | DDR5-5600 | 
Note that DDR5 has 32-bit memory channels instead of 64-bit memory channels
as the previous memory generations.

## Slide 83: 2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (9)
Preserving the per-core memory bandwidth while core counts grow -1
While core counts of Intel’s Core 2-based client processors have grown from
2 to 24 Intel did not raise the number of memory channels.
The reason for hold on just two memory channels is the fact that memory rates
could be raised fast enough to sustain more or less the per-core memory
bandwidth vs. its value provided in the 1. gen., as the next Table indicates.

## Slide 84
2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (10)
The rate of raising memory speeds in Core 2-based client processors -1
Gen. | Seg-ment | Attaching memory | Processor | Techno- logy | Max core count | Date of intro. | Socket | MCH/PCH | Mem. speed (up to) | Mem. channels
1. | M D | Attaching memory to the NB | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
 | D |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series | DDR3-1067 | 
 | D |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series | DDR3-1067 | 
 | D | Attaching memory to the processor die | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series | DDR3-1333 | 
 | M D |  | Westmere (M: Arrandale) D: Clarkdale/ | 32 nm | 2C+G | 1/2010 | M:BGA 1288 D:LGA 1156 | 5 Series |  | 
2. | M D |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | M: PGA 988 D: LGA 1155 | 6 series | DDR3-1333 | 
3. | M D |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 |  | 7 series | DDR3-1600 | 
4. | M D |  | Haswell | 22 nm | 4C+G | 6/2013 | M: BGA 1168 D: LGA 1150 | 8 Series | DDR3-1600 | 
4. | D |  | Haswell Refr. | 22 nm | 4C+G | 5/2014 |  | 9 Series | DDR3-1666 | 
5. | M D |  | Broadwell | 14 nm | 4C+G | 6/2015 |  | 9 Series | DDR3-1866 | 
 |  |  | Skylake | 14 nm | 4C+G | 10/2015 | M: BGA 1356 D: LGA 1151 | Series | DDR4-2133 | 
6. | M D |  |  |  |  |  |  |  |  | 
7. | M D |  | Kaby Lake | 14 nm | 4C + G | 8/2016 |  | 200 Series | DDR4-2400 | 
8. | M D |  | Coffee Lake | 14 nm | 6C +G | 10/2017 | M: BGA 1440 D: LGA 1151 | 300 Series | DDR4-2666 | 
8. | M |  | Amber Lake | 14 nm | 2C+G | 8/2018 | BGA 1515 | 300 Series | LPDDR3-2133 | 
8. | M |  | Whiskey Lake | 14 nm | 4C+G | 8/2018 | BGA 1528 | 300 Series | DDR4-2400 | 
9. | D |  |  |  |  |  |  |  |  | 
 |  |  | Coffee Lake R. | 14 nm | 8C +G | 10/2018 | LGA 1151 | 300 Series | DDR4-2666 | 
 |  |  | Comet Lake | 14 nm | 10C +G | 8/2019 | BGA 1528 LGA 1200 | 400 Series | DDR4-2666 | 
10. | M D |  |  |  |  |  |  |  |  | 
11. | D |  | Rocket Lake | 14 nm | 8C +G | 3/2021 | LGA 1200 | 400 Series | DDR4-3200 | 

## Slide 85: 2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (11)
The rate of raising memory speeds in Core 2-based client processors -2
Gen. | Seg-ment | Attaching memory | Processor | Techno- logy | Max. core count | Date of intro. | Socket | PCH | Mem. speed (up to) | Mem. channels
8. | M | Attaching memory to the processor die | Cannon Lake | 10 nm | 2C | 5/2018 | BGA | n.a. | DDR4-2400 | 2
10. | M |  | Ice Lake | 10 nm | 4C+G | 7/2019 | Y: BGA 1377 U: BGA 1526 | 300-series | DDR4-3733 | 
11. | M D |  | Tiger Lake | 10 nm | 8C+G | 09/2020 | UP3: BGA 1449 UP4: BGA 1598 B/H: BGA 1787 | 400-series | LPDDR4x-4267 LPDDR5x-5400 | 
12. | M D |  | Alder Lake | 10 nm (Intel 7) | 8C+8C+G | 11/2021 | M: BGA 1744 D: LGA 1700 | 600-series | DDR5-4800 | 4x 32-bit
13 | M D |  | Raptor Lake | 10 nm (Intel 7) | 8C+16C+G | 09/2022 | LGA 1700 | 700-series | DDR5-5600 | 

## Slide 86: 2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (12)

1600
3200
1333
1862
2133
2400
2666
2793
Year
2010
09
11
12
13
14
16
2015
17
18
2020
19
*
*
*
*
*
*
*
*
*
SB
IB
HW
SKL4
KBL
CFL
ICL
TGL
4266
08
1066
PN
*
*
N1
N2
DDR4 ~ 2x /8 years
DDR3 ~ 2x /8 years
3458
The rate of raising memory speeds in Core 2-based client processors -3
MT/s
BW
3733
As the Figure indicates DDR3/4 memory speeds could be doubles roughly in every 8 years.

## Slide 87: 2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (13)
Generation | Introduced | Processor line | Max. core count | Memory rate | Per-core memory bandwidth GB/s
1. | 06/2006 | Core 2 | 2 | DDR2-800 | 6.4
 | 06/2009 | Nehalem | 4 | DDR3-1333 | 5.4
8. | 10/2017 | Coffee Lake | 6 | DDR4-2666 | 7.2
9. | 10/20118 | Coffee Lake R. | 8 | DDR4-2666 | 5.4
10. | 08/2019 | Comet Lake | 10 | DDR4-2666 | 4.2
12. | 11/2021 | Alder Lake | 8+824 | DDR5-4800 | 4.8
13. | 10/2022 | Raptor Lake | 8+16 | DDR5-5600 | 3.7
Table: Per-core memory bandwidth of client processors with increased core counts
Preserving the per-core memory bandwidth while core counts grow -1

## Slide 88: 2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (14)
The way of attaching memory to Core 2-based client platforms -1
Options for attaching memory to platforms
Options for attaching memory to platforms
Attaching memory
to the NB
(MC is integrated
into the NB)
Attaching memory
to the processor
(MC is integrated
onto the processor die)
NB
SB
FSB
Processor
NB
SB
FSB
Processor r
Memory
Memory
MC
MC
NB: North Bridge
SB: South Bridge

## Slide 89: 2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (14b)
PCI
Memory bandwidth benefit while attaching memory to a 4S server directly via
the MCH or directly to the processor rather than via the MCH (based on [228])
As the Figure shows, direct attaching memory to the processor greatly relieves bandwidth
limitations of platforms where memory is attached via the MCH.

## Slide 90
2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (15)
The way of attaching memory to Intel’s Core 2-based client platforms -2
Gen. | Seg-ment | Attaching memory | Processor | Techno- logy | Max core count | Date of intro. | Socket | MCH/PCH | Mem. speed (up to) | Mem. channels
1. | M D | Attaching memory to the NB | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
 | D |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series | DDR3-1067 | 
 | D |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series | DDR3-1067 | 
 | D | Attaching memory to the processor die | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series | DDR3-1333 | 
 | M D |  | Westmere (M: Arrandale) D: Clarkdale/ | 32 nm | 2C+G | 1/2010 | M:BGA 1288 D:LGA 1156 | 5 Series |  | 
2. | M D |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | M: PGA 988 D: LGA 1155 | 6 series | DDR3-1333 | 
3. | M D |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 |  | 7 series | DDR3-1600 | 
4. | M D |  | Haswell | 22 nm | 4C+G | 6/2013 | M: BGA 1168 D: LGA 1150 | 8 Series | DDR3-1600 | 
4. | D |  | Haswell Refr. | 22 nm | 4C+G | 5/2014 |  | 9 Series | DDR3-1666 | 
5. | M D |  | Broadwell | 14 nm | 4C+G | 6/2015 |  | 9 Series | DDR3-1866 | 
 |  |  | Skylake | 14 nm | 4C+G | 10/2015 | M: BGA 1356 D: LGA 1151 | Series | DDR4-2133 | 
6. | M D |  |  |  |  |  |  |  |  | 
7. | M D |  | Kaby Lake | 14 nm | 4C + G | 8/2016 |  | 200 Series | DDR4-2400 | 
8. | M D |  | Coffee Lake | 14 nm | 6C +G | 10/2017 | M: BGA 1440 D: LGA 1151 | 300 Series | DDR4-2666 | 
8. | M |  | Amber Lake | 14 nm | 2C+G | 8/2018 | BGA 1515 | 300 Series | LPDDR3-2133 | 
8. | M |  | Whiskey Lake | 14 nm | 4C+G | 8/2018 | BGA 1528 | 300 Series | DDR4-2400 | 
9. | D |  |  |  |  |  |  |  |  | 
 |  |  | Coffee Lake R. | 14 nm | 8C +G | 10/2018 | LGA 1151 | 300 Series | DDR4-2666 | 
 |  |  | Comet Lake | 14 nm | 10C +G | 8/2019 | BGA 1528 LGA 1200 | 400 Series | DDR4-2666 | 
10. | M D |  |  |  |  |  |  |  |  | 
11. | D |  | Rocket Lake | 14 nm | 8C +G | 3/2021 | LGA 1200 | 400 Series | DDR4-3200 | 

## Slide 91: 2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (16)
The way of attaching memory to Intel’s Core 2-based client platforms -3
Gen. | Seg-ment | Attaching memory | Processor | Techno- logy | Max. core count | Date of intro. | Socket | PCH | Mem. speed (up to) | Mem. channels
8. | M | Attaching memory to the processor die | Cannon Lake | 10 nm | 2C | 5/2018 | BGA | n.a. | DDR4-2400 | 2
10. | M |  | Ice Lake | 10 nm | 4C+G | 7/2019 | Y: BGA 1377 U: BGA 1526 | 300-series | DDR4-3733 | 
11. | M D |  | Tiger Lake | 10 nm | 8C+G | 09/2020 | UP3: BGA 1449 UP4: BGA 1598 B/H: BGA 1787 | 400-series | LPDDR4x-4267 LPDDR5x-5400 | 
12. | M D |  | Alder Lake | 10 nm (Intel 7) | 8C+8C+G | 11/2021 | M: BGA 1744 D: LGA 1700 | 600-series | DDR5-4800 | 4x 32-bit
13 | M D |  | Raptor Lake | 10 nm (Intel 7) | 8C+16C+G | 09/2022 | LGA 1700 | 700-series | DDR5-5600 | 

## Slide 92: 2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (17)
The way of attaching memory to *Core 2-based client platforms -4
As the previous Tables show, in early Core 2-based client platforms memory was
attached to the NB, but soon, beginning with the Nehalem processors Intel began
attaching memory immediately to the processor die.
Notes
The Table providing an overview of Intel’s Core 2-based client processors doesn’t
enlist 1. gen. Nehalem-based client processors, since this line targeted actually
servers, nevertheless by deactivating server related parts of the dies Intel sold
1. gen. Nehalem dies also as high-performance DT processors (in 2008).
2) Intel was quite late in switching to direct attached memory, as the subsequent
retrospect reveals.

## Slide 93: 2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (18)
The way of attaching memory to Core 2-based client platforms -5
Options for attaching memory to platforms
Attaching memory to the processor die
Attaching memory to the NB
POWER4 (2C) (2001)
POWER5 (2C) (2005)
and subsequent POWER families
Montecito (2C) (2006)
Opteron server lines (2C) (2003)
and all subsequent AMD lines
Core 2 Duo line (2C) (2006)
and all preceding Intel lines
Core 2 Quad line (2x2C) (2006/2007)
Penryn line (2x2C) (2008)
Nehalem lines (4) (2008)
and all subsequent Intel lines
Examples
Tukwila (4C) (2010)
AMD’s K7 lines (1C)
(1999-2003)
UltraSPARC III (2001)
and all subsequent Sun models
UltraSPARC II (1C) (~1997)
HP PA-7100 (1992)
HP PA-7150 (1994)
and subsequent PA models
HP PA-7000 (1991)

## Slide 94: 2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (19)
a) Evolution of core counts
b) Implementing dual memory channels
Summing up key issues of the evolution of Intel’s Core 2-based client processors -1
Following the advances of the IC technology, maximum core counts of Intel’s
client processors rose already in 2007 to 4 and remained so roughly for 10 years,
as most earlier applications did not offer much more parallelism that might have
been utilized (see the next Figure).
This situation has changed however, when AMD entered the market with 8-core
and later 16-core (GPU-less) Zen processors in 2017 and 2020, respectively.
To encounter the competition, Intel raised the core count of its client processors
first to 6 then to 8 subsequently to 10, and in 2022 even to 24 in their 13th gen.
Raptor Lake processor line.
The reason for holding on just two memory channels is the fact that memory rates
could be raised fast enough to sustain more or less the per-core memory
bandwidth vs. its early value provided in the 1. gen.
Despite rising core counts from 2 to 24 Intel remained by implementing dual
memory channels.
Note that DDR5 has 32-bit memory channels instead of 64-bit memory channels
as the previous memory generations.

## Slide 95: 2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (20)
Summing up key issues of the evolution of Intel’s Core 2-based client processors -2
Note that typically, Intel’s mobile (actually laptop) oriented Core 2 processors have
BGA sockets whereas desktop processors LGA (in early lines PGA) sockets.

## Slide 96: 2.2 Evolution of core counts and memory support in Intel’s Core 2-based client line (21)
Options for attaching memory to platforms
Attaching memory
to the NB
(MC is integrated
into the NB)
Attaching memory
to the processor
(MC is integrated
onto the processor die)
NB
SB
FSB
Processor
NB
SB
FSB
Processor r
Memory
Memory
MC
MC
NB: North Bridge
SB: South Bridge
c) The rate of raising memory speeds in Intel’s Core 2-based client processors
As shown, memory speeds in Intel’s Core 2-based client processors could be
doubled roughly in every 8 years.
d) The way of attaching memory to Intel’s Core 2-based client platforms
Summing up key issues of the evolution of Intel’s Core 2-based client processors -3
In early Core 2-based client platforms memory was attached to the NB, but
beginning with the Nehalem line Intel began attaching memory immediately
to the processor die in 2008.

## Slide 97
2.3 Evolution of key features of integrated graphics
in Intel’s Core 2 line
2.3.1 Overview of the evolution of integrated graphics
in the Core 2 line
2.3.3 Overview of the implementation of integrated graphics
in the Core 2 line
2.3.4 Evolution of the performance of integrated graphics
in the Core 2 line
2.3.2 Case example: The 12th gen. Xe LP GPU of 11th gen.
Tiger Lake processors
Section 2.3.3 is only optional reading.
Notes: 97

## Slide 98
2.3.1 Overview of the evolution of integrated graphics
in the Core 2 line
Notes: 98

## Slide 99: 2.3.1 Overview of the evolution of integrated graphics in the Core 2 line (1)
2.3.1 Overview of the evolution of integrated graphics in the Core 2 line
For their Core 2 processors Intel developed two GPU families:
the HD family and
the Xe family.
Overview of Intel’s integrated graphics families -1
Intel’s client processors for laptops and general purpose desktops typically include
integrated GPUs whereas desktop processors designed for gaming usually have
only discrete graphics and do not include integrated GPUs.
Similarly, HEDTs and servers do not need integrated GPUs.

## Slide 100: 2.3.1 Overview of the evolution of integrated graphics in the Core 2 line (2)
a) Intel’s HD graphics family -1
The HD family of GPUs was introduced along with the Westmere line in 2010,
nevertheless it was still in package integrated graphics including separate CPU
and graphics dies, enclosed into a package.

## Slide 101
Intel Core generation | Arch. gen. | Graphics gen. | HD/Xe | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version at intro.
Westmere | -- | 5th (Ironlake) | HD | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 2nd | 6th |  | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  |  |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 3rd | 7th |  | HD 2500 | GT1 | 1 (2x3? EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  |  |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 4th | 7.5th |  | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  |  |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  |  |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 5th | 8th |  | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  |  |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  |  |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 6th | 9th |  | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  |  |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  |  |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  |  |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  |  |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  |  |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Overview of Intel’s graphics families -1 (based on [20])
2.3.1 Overview of the evolution of integrated graphics in the Core 2 line (3)

## Slide 102: 2.3.1 Overview of the evolution of integrated graphics in the Core 2 line (4)
a) Intel’s HD graphics family -2
Next the GPU became integrated onto the processor die in the 2nd gen. Sandy Bridge
line in 2011.
Intel implemented HD graphics with continuous enhancements in their processors
manufactured on up to (and including) the 14 nm technology, at last in the Comet Lake
line (2019), however lastly, renamed to UHD graphics, as the following Tables indicate.

## Slide 103
Intel Core generation | Arch. gen. | Graphics gen. | HD/Xe | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version at intro.
Westmere | -- | 5th (Ironlake) | HD | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 2nd | 6th |  | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  |  |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 3rd | 7th |  | HD 2500 | GT1 | 1 (2x3? EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  |  |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 4th | 7.5th |  | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  |  |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  |  |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 5th | 8th |  | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  |  |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  |  |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 6th | 9th |  | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  |  |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  |  |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  |  |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  |  |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  |  |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Overview of Intel’s graphics families -2 (based on [20])
2.3.1 Overview of the evolution of integrated graphics in the Core 2 line (5)

## Slide 104
Overview of Intel’s graphics families -3 (based on [20])
2.3.1 Overview of the evolution of integrated graphics in the Core 2 line (6)
Intel Core generation | Arch. gen. | Graphics gen. | HD/Xe | Models | Graphics Technology level | No. of HD graphics slices/Xe subslices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version at intro.
Kaby Lake | 7th | 9th | HD | HD 610 | GT1 | 1 | 12 | -- | 4.5 | 12 | 2.1?
 |  |  |  | HD 615 | GT2 | 1 | 24 |  |  |  | 
 |  |  |  | HD 620 |  |  |  |  |  |  | 
 |  |  |  | HD 630 |  |  |  |  |  |  | 
 |  |  |  | HD 640 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  |  |  | HD 650 |  |  |  | 64 MB |  |  | 
Kaby Lake Refr. to Comet Lake | 8th - 10th | 9th |  | UHD 610 | GT1 | 1 | 12 | n.a. |  |  | 
 |  |  |  | UHD 615 | GT2 | 1 | 24 |  |  |  | 
 |  |  |  | UHD 617 |  |  |  |  |  |  | 
 |  |  |  | UHD 620 |  |  |  |  |  |  | 
 |  |  |  | UHD 630 |  |  |  |  |  |  | 
 |  |  |  | UHD 645 | GT3 | 2 | 48 |  |  |  | 
 |  |  |  | UHD 655 |  |  |  |  |  |  | 
Ice Lake | 10th | 11th | Xe | Iris Xe | G1 | 4 | 32 | n.a. | 4.6? | 12.1 | 2.1
 |  |  |  | Iris Xe | G4 | 6 | 48 |  |  |  | 
 |  |  |  | Iris Xe | G7 | 8 | 64 |  |  |  | 
Tiger Lake | 11th | 12th |  | Iris Xe LP | G1 | 2 | 32 | n.a. |  |  | 3.0
 |  |  |  | Iris Xe LP | G4 | 3 | 48 |  |  |  | 
 |  |  |  | Iris Xe LP | G7 | 5 | 80 |  |  |  | 
 |  |  |  | Iris Xe LP | G7 | 6 | 96 |  |  |  | 
Alder Lake-S | 12th | 12th |  | Iris Xe UHD 770 | na. | na. | 80/96 32/64 | n.a. |  |  | 

## Slide 105: 2.3.1 Overview of the evolution of integrated graphics in the Core 2 line (7)
b) Intel’s Xe graphics family
The Xe family of GPUs is a complete re-design targeting all major market segments
from client processors used for gaming up to data centers with HPC workloads.
Remark
AMD’s chief graphics designer, Raja Koduri left the firm and joined Intel in 2017
to became the lead graphics architect.
The Xe graphics family was designed under his leadership.
In client processors Xe graphics appeared along with the 10 nm processors, first
in Intel’s 10th generation Ice Lake line in 2019, named as the 11th gen. Iris Xe graphics,
as indicated in the next Table.

## Slide 106
Overview of Intel’s graphics families -4 (based on [20])
2.3.1 Overview of the evolution of integrated graphics in the Core 2 line (8)
Intel Core generation | Arch. gen. | Graphics gen. | HD/Xe | Models | Graphics Technology level | No. of HD graphics slices/Xe subslices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version at intro.
Kaby Lake | 7th | 9th | HD | HD 610 | GT1 | 1 | 12 | -- | 4.5 | 12 | 2.1?
 |  |  |  | HD 615 | GT2 | 1 | 24 |  |  |  | 
 |  |  |  | HD 620 |  |  |  |  |  |  | 
 |  |  |  | HD 630 |  |  |  |  |  |  | 
 |  |  |  | HD 640 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  |  |  | HD 650 |  |  |  | 64 MB |  |  | 
Kaby Lake Refr. to Comet Lake | 8th - 10th | 9th |  | UHD 610 | GT1 | 1 | 12 | n.a. |  |  | 
 |  |  |  | UHD 615 | GT2 | 1 | 24 |  |  |  | 
 |  |  |  | UHD 617 |  |  |  |  |  |  | 
 |  |  |  | UHD 620 |  |  |  |  |  |  | 
 |  |  |  | UHD 630 |  |  |  |  |  |  | 
 |  |  |  | UHD 645 | GT3 | 2 | 48 |  |  |  | 
 |  |  |  | UHD 655 |  |  |  |  |  |  | 
Ice Lake | 10th | 11th | Xe | Iris Xe | G1 | 4 | 32 | n.a. | 4.6? | 12.1 | 2.1
 |  |  |  | Iris Xe | G4 | 6 | 48 |  |  |  | 
 |  |  |  | Iris Xe | G7 | 8 | 64 |  |  |  | 
Tiger Lake | 11th | 12th |  | Iris Xe LP | G1 | 2 | 32 | n.a. |  |  | 3.0
 |  |  |  | Iris Xe LP | G4 | 3 | 48 |  |  |  | 
 |  |  |  | Iris Xe LP | G7 | 5 | 80 |  |  |  | 
 |  |  |  | Iris Xe LP | G7 | 6 | 96 |  |  |  | 
Alder Lake-S | 12th | 12th |  | Iris Xe UHD 770 | na. | na. | 80/96 32/64 | n.a. |  |  | 

## Slide 107
Intel Core generation | Arch. gen. | Graphics gen. | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version at intro.
Westmere | -- | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 2nd | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 3rd | 7th | HD 2500 | GT1 | 1 (2x3? EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 4th | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 5th | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 6th | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Designation of Intel’s graphics generations -1 (based on [20])
2.3.1 Overview of the evolution of integrated graphics in the Core 2 line (9)

## Slide 108: 2.3.1 Overview of the evolution of integrated graphics in the Core 2 line (10)
Designation of Intel’s graphics generations -2
The reason for this inconsistency is that Intel began designing GPUs quite early, but
first implementations were stand alone chips (1998) whereas subsequent GPUs were
integrated into the NB (GMCH) from 1999 on.
These discrete graphics implementations were called the 1st to 4th generations, followed
by the 5th generation which was package integrated graphics where both the
GPU and CPU dies were integrated into the same package, in the Westmere line of
processors (2010).
Intel’s microarchitectures and graphics generations are designated differently,
for example, Intel’s first on-die integrated graphics was implemented in the
2nd gen. Sandy Bridge line in 2011 and became Intel’s 6th gen. HD graphics, (as indicated
in the previous Table).

## Slide 109
Intel Core generation | Arch. gen. | Graphics gen. | Models | Graphics Technology level | No. of graphics slices/Xe subslices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version at intro.
Kaby Lake | 7th | 9th | HD 610 | GT1 | 1 | 12 | -- | 4.5 | 12 | 2.1?
 |  |  | HD 615 | GT2 | 1 | 24 |  |  |  | 
 |  |  | HD 620 |  |  |  |  |  |  | 
 |  |  | HD 630 |  |  |  |  |  |  | 
 |  |  | HD 640 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  |  | HD 650 |  |  |  | 64 MB |  |  | 
Kaby Lake Refr. to Comet Lake | 8th - 10th | 9th | UHD 610 | GT1 | 1 | 12 | n.a. |  |  | 
 |  |  | UHD 615 | GT2 | 1 | 24 |  |  |  | 
 |  |  | UHD 617 |  |  |  |  |  |  | 
 |  |  | UHD 620 |  |  |  |  |  |  | 
 |  |  | UHD 630 |  |  |  |  |  |  | 
 |  |  | UHD 645 | GT3 | 2 | 48 |  |  |  | 
 |  |  | UHD 655 |  |  |  |  |  |  | 
Ice Lake | 10th | 11th | Iris Xe | G1 | 4 | 32 | n.a. | 4.6 | 12.1 | 2.1
 |  |  | Iris Xe | G4 | 6 | 48 |  |  |  | 
 |  |  | Iris Xe | G7 | 8 | 64 |  |  |  | 
Tiger Lake | 11th | 12th | Iris Xe LP | G1 | 2 | 32 | n.a. |  |  | 3.0
 |  |  | Iris Xe LP | G4 | 3 | 48 |  |  |  | 
 |  |  | Iris Xe LP | G7 | 5 | 80 |  |  |  | 
 |  |  | Iris Xe LP | G7 | 6 | 96 |  |  |  | 
Alder Lake | 12th | 12th | Iris Xe UHD 770 | na. | na. | 80/96 32/64 | n.a. |  |  | 
Designation of Intel’s graphics generations -3 (based on [20])
2.3.1 Overview of the evolution of integrated graphics in the Core 2 line (11)

## Slide 110: 2.3.1 Overview of the evolution of integrated graphics in the Core 2 line (12)
Enhanced support of graphics APIs -1
Subsequent graphics generations provide more or more support for advanced
graphics APIs, as the next Tables indicate.

## Slide 111: 2.3.1 Overview of the evolution of integrated graphics in the Core 2 line (13)
Intel Core generation | Arch. gen. | Graphics gen. | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Westmere | -- | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 2nd | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 3rd | 7th | HD 2500 | GT1 | 1 (2x3? EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 4th | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 5th | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 6th | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Support of graphics APIs -2

## Slide 112: 2.3.1 Overview of the evolution of integrated graphics in the Core 2 line (14)
Intel Core generation | Arch. gen. | Graphics gen. | Models | Graphics Technology level | No. of graphics slices/Xe subslices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Kaby Lake | 7th | 9th | HD 610 | GT1 | 1 | 12 | -- | 4.5 | 12 | 2.1?
 |  |  | HD 615 | GT2 | 1 | 24 |  |  |  | 
 |  |  | HD 620 |  |  |  |  |  |  | 
 |  |  | HD 630 |  |  |  |  |  |  | 
 |  |  | HD 640 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  |  | HD 650 |  |  |  | 64 MB |  |  | 
Kaby Lake Refr. to Comet Lake | 8th - 10th | 9th | UHD 610 | GT1 | 1 | 12 | n.a. |  |  | 
 |  |  | UHD 615 | GT2 | 1 | 24 |  |  |  | 
 |  |  | UHD 617 |  |  |  |  |  |  | 
 |  |  | UHD 620 |  |  |  |  |  |  | 
 |  |  | UHD 630 |  |  |  |  |  |  | 
 |  |  | UHD 645 | GT3 | 2 | 48 |  |  |  | 
 |  |  | UHD 655 |  |  |  |  |  |  | 
Ice Lake | 10th | 11th | Iris Xe | G1 | 4 | 32 | n.a. | 4.6 | 12.1 | 2.1
 |  |  | Iris Xe | G4 | 6 | 48 |  |  |  | 
 |  |  | Iris Xe | G7 | 8 | 64 |  |  |  | 
Tiger Lake | 11th | 12th | Iris Xe LP | G1 | 2 | 32 | n.a. |  |  | 3.0
 |  |  | Iris Xe LP | G4 | 3 | 48 |  |  |  | 
 |  |  | Iris Xe LP | G7 | 5 | 80 |  |  |  | 
 |  |  | Iris Xe LP | G7 | 6 | 96 |  |  |  | 
Alder Lake | 12th | 12th | Iris Xe UHD 770 | na. | na. | 80/96 32/64 | n.a. |  |  | 
Support of graphics APIs -3

## Slide 113
2.3.2 Case example: The 12th gen. Xe LP GPU
of 11th gen. Tiger Lake processors
Notes: 113

## Slide 114: 2.3.2 Case example: The 12th gen. Xe LP GPU of 11th gen. Tiger Lake processors (1)
Intel’s 12th gen. Xe LP EUs are built up of modules where each module includes dual
subslices with shared thread control [23].
In the Figure above (G7 implementation) there are three modules with 6 subslices.
2.3.2 Case example: The 12th gen. Xe LP GPU of 11th gen. Tiger Lake processors

## Slide 115: 2.3.2 Case example: The 12th gen. Xe LP GPU of 11th gen. Tiger Lake processors (2)
Graphics subslices of 12th gen. Xe LP GPUs of 11th gen. Tiger Lake processors [22]
Figure: Graphics subslice of Intel’s
12th gen. Xe LP GPUs [22]
Subslices are subunits of slices including
among others 16 EUs (Execution Units)
for performing FX/FP computations.
There are different numbers of subslices
in Intel’s different processor models,
e.g. 2 - 6 in 12th gen. Xe LP GPUs, as seen
before.
Consequently, 12th gen. Xe LP GPUs may
include up to 96 EUs.

## Slide 116: 2.3.2 Case example: The 12th gen. Xe LP GPU of 11th gen. Tiger Lake processors (3)
Layout of 12th gen. graphics EUs (actually 2 EUs) of Tiger Lake processors [22]
On the IP 0 there are two 8-wide (8x32-bit)
SIMD ALUs (an FP and an FX ALU) available,
they operate exclusively and can perform up to
whereas on the IP 1 there is an
Extended Math (EM) unit available,
that can perform up to two
Extended Math (EM) operations
(to calculate trigonometric functions etc.)
8 FP32, 16 FP16 FMA operations or
8 FX32, 16 FX16, 32 FX8 FMA operations,

## Slide 117: 2.3.2 Case example: The 12th gen. Xe LP GPU of 11th gen. Tiger Lake processors (4)
Computing capabilities of Intel’s 11th and 12th gen.EUs (operations/clock/EU) |  | 
 | Xe LP (Gen 12) | Xe (Gen11)
FP32 | 16 | 16
FP16 | 32 | 32
FX32 | 8 | 4
FX16 | 32 | 16
FX8 (INT8) | 64 | N/A
Data in the above Table take into account that the EUs may perform FMA
(Fused Multiply-Add) operations.
Summing up the computing capabilities of 12th gen. graphics EUs [23]

## Slide 118
2.3.2 Overview of the implementation of integrated graphics in the Core 2 line
Optional reading, not part of the exam.
Notes: 118

## Slide 119: 2.3.3 Overview of the implementation of integrated graphics in the Core 2 line (1)
2.3.3 Overview of the implementation of integrated graphics in the Core 2 line
Slice
Intel’s GPUs are built up of graphics slices.
Graphics slices, as seen below, are complete GPU units that can be multiplied to build a GPU.
HD graphics typically includes up to 3 slices whereas Xe graphics, implemented
in client processors, only a single slice, up to now (03/2022).
Figures: Example of an Xe-based
11th gen. graphics slice with 8 subslices
used in the 10 nm 10th gen. Ice Lake
line (2019). [21]

## Slide 120: 2.3.3 Overview of the implementation of integrated graphics in the Core 2 line (2)
Remark
In Intel’s HD graphics the number of graphics slices is given by the GTL (Graphics
Technology Level) identifier.
GTL 2 indicates a single graphics slide, GTL3 two slices, GTL4 three slices,
whereas GTL1 indicates a single slice with less EUs per subslice than provided
by GTL2-GTL4 implementations.

## Slide 121: 2.3.3 Overview of the implementation of integrated graphics in the Core 2 line (3)
Implementation of Intel’s graphics – graphics subslices
Figures: Example of an Xe-based
11th gen. graphics slice and subslice
used in the 10 nm 10th gen. Ice Lake
line (2019). [21]
Slice
Subslices are subunits of slices including EUs (Execution Units) for performing
FX/FP computations.
There are different number of subslices in Intel’s graphics implementations, 2 or 3
in the HD graphics and 2 – 8 in Xe graphics, e.g. 8 in 11th gen. graphics, see below.

## Slide 122: 2.3.3 Overview of the implementation of integrated graphics in the Core 2 line (4)
Indication of the number of subslices in the Xe graphics
In their Xe graphics Intel introduced the G identifiers (tags) (G1/G4/G7) for
stating the number of subslices included in a graphics slice.
G-identifiers (tags) in 11th and 12th gen. graphics are interpreted as follows:
Designation | Level | Subslices | EUs
Iris Xe | G1 | 4 | 32
Iris Xe | G4 | 6 | 48
Iris Xe | G7 | 8 | 64
Table: Number of subslices and EUs in Intel’s 11th gen. Xe graphics (implemented
in in the 10th gen. Ice Lake line
G-identifiers are attached as tags to the model designations in the 11th gen Xe (Ice Lake line) and 12th gen. Xe LP graphics (Tiger Lake lines) but no more in the
12th gen. graphics (12th gen. Alder Lake line).
Designation | Level | Subslices | EUs
Iris Xe LP | G1 | 2 | 32
Iris Xe LP | G4 | 3 | 48
Iris Xe LP | G7 | 4 | 64
Iris Xe LP | G7 | 5 | 80

## Slide 123: 2.3.3 Overview of the implementation of integrated graphics in the Core 2 line (5)
Layout of subslices in Intel’s Xe/Xe LP graphics
Subslices of the 11th gen. Xe graphics (10th gen. Ice Lake) and 12th gen. Xe LP
graphics (Tiger Lake) are built up differently; the main difference is that 11th gen. Xe
subslices have 8 EUs whereas 12th gen. Xe LP subslices 16 EUs, as discussed next.

## Slide 124: 2.3.3 Overview of the implementation of integrated graphics in the Core 2 line (6)
Layout of 11th gen. subslices in the Xe graphics (implemented in the
10th gen. Ice Lake line)
Figure: Subslice of an 11th gen. GPU
used in the 10th gen. Ice Lake line [21]
Key parts of an 11th gen. subslice
8 EUs (to be described subsequently) and
an SLM (Shared Local Memory of 64 kB
accessible from all EUs holding memory data
that might be shared between all EUs of the
subslice.

## Slide 125: 2.3.3 Overview of the implementation of integrated graphics in the Core 2 line (7)
Layout of 12th gen. Xe LP (Tiger Lake) subslices vs. 11th gen. (Ice Lake line) subslices
11th gen.
[21]
12th gen.
[22]
12th gen. subslices include 16 EUs rather than 8 as jn the previous 11th generation
graphics.

## Slide 126: 2.3.3 Overview of the implementation of integrated graphics in the Core 2 line (8)
Layout of EUs in Xe/Xe LP graphics
11th gen. and 12th gen. EUs are built up differently.
11th gen. Xe EUs have dual SIMD units capable of performing 4-wide (4x32-bit)
FX/FP FMA (Fused Multiply-Add) and 2-wide EM (Extended Math) operations.
By contrast, 12th gen. Xe LP EUs are built up as modules including dual EUs with
shared thread control and dual SIMD units capable of performing 8-wide (8x32-bit)
FP/FX FMA and and 2-wide EM (Extended Math) operations, as discussed next.

## Slide 127: 2.3.3 Overview of the implementation of integrated graphics in the Core 2 line (9)
Layout of an 11th gen. EU of the Xe LP graphics (implemented in the 11th gen.
Tiger Lake line) [22]
Main parts of an 11th gen. graphics EU:
dual SIMD ALUs
a register file (GFR)
a Branch and a Send (IO) Unit and
thread control that may issue up to one
instruction to each unit in each clock cycle
Each EU is 7-way multithreaded.
Each thread has 128 256-bit long general purpose registers (i.e. 4KB per thread
or 28 KB per EU).
Each GPR register can hold up to 8 32-bit FP or FX data or even up to 16 16-bit
FP or FX data.
Xe EU
up to 4 FP32/8 FP16 FMA operations or
up to 4 FX32/8 FX16 FMA operations,
The SIMD ALU on the IP 0 can perform
up to 4 FP32/8 FP16 FMA operations or
whereas the other SIMD ALU on the IP1:
dual Extended Math (EM) operations
(to calculate trigonometric functions etc.).
Remark EUs of the previous HD graphics are built up basically in the same way.

## Slide 128: 2.3.3 Overview of the implementation of integrated graphics in the Core 2 line (10)
Layout of 12th gen. graphics EUs vs. 11th gen. EUs -1 [22]
12th gen. EUs are implemented as modules with shared thread control and branch
unit, as shown below.
Xe EU
As shown, 12th gen. FP and FX units are 8-wide whereas 11th gen FP and FX units
only 4 wide, this results in the same FP performance but doubles FX performance.
12th gen. FP and FX units are able to perform also FX8 operations, which is useful
in speeding up AI applications.
In addition, EM operations do not more block the execution of FP operations, nevertheless either an FP or an FX operation can be issued per cycle.

## Slide 129: 2.3.3 Overview of the implementation of integrated graphics in the Core 2 line (11)
up to 4 FP32, 8 FP16 FMA operations or
up to 4 FX32, 8 FX16 FMA operations,
The SIMD ALU on IP 0 can perform
up to 4 FP32, 8 FP16 FMA operations or
whereas the other SIMD ALU on IP1:
dual Extended Math (EM) operations
(to calculate trigonometric functions etc.)
up to 8 FP32, 16 FP16 FMA operations or
up to 8 FX32, 16 FX16, 32 FX8 FMA operations,
The main SIMD ALU on IP 0 can perform
whereas the EM ALU on IP 1:
dual Extended Math (EM) operations
(to calculate trigonometric functions etc.)
Xe EU
Xe EU
Contrasting the computing capabilities of 11th and 12th gen. graphics EUs -1 [22]

## Slide 130: 2.3.3 Overview of the implementation of integrated graphics in the Core 2 line (12)
Computing capabilities of Intel’s 11th and 12th gen.EUs (operations/clock/EU) |  | 
 | Xe LP (Gen 12) | Xe (Gen11)
FP32 | 16 | 16
FP16 | 32 | 32
FX32 | 8 | 4
FX16 | 32 | 16
FX8 (INT8) | 64 | N/A
Data in the above Table take into account that the EUs may perform FMA
(Fused Multiply-Add) operations.
Contrasting the computing capabilities of 11th and 12th gen. graphics Eus -2 [23]

## Slide 131: 2.3.3 Overview of the implementation of integrated graphics in the Core 2 line (13)
The 12th gen. Xe LP GPU of Tiger Lake processors -1 [23]
It has up to 6 subslices
(model dependent)
16 EUs/subslice
i.e. 96 EUs/slice
(up from 64)

## Slide 132
2.3.4 Evolution of the performance of integrated graphics in the Core 2 line
Notes: 132

## Slide 133: 2.3.4 Evolution of the performance of integrated graphics in the Core 2 line (1)
Raising the max. number of graphics EUs in GPUs of Core 2 processors -2
No of EUs
(log scale)
2006
2008
2010
2012
2014
2016
Year
2018
2020
2022
*
*
*
*
*
*
12
16
40
48
72
96
Sandy
Bridge
Ivy
Bridge
Haswell
Broadwell
Ice Lake
Tiger Lake

## Slide 134: 2.3.4 Evolution of the performance of integrated graphics in the Core 2 line (2)
Raising the max. number of graphics EUs in GPUs of Core 2 processors -1
As the Figure above shows, Intel raised the max number of graphics EUs in their
GPUs immensely, from 12 (in the Sandy Bridge) to 96 (in the Tiger Lake) in less
than 10 years, this is roughly a 10-fold increase in 10 years.
The graphics performance is expected to scale more or less linearly with the
number of EUs provided in the GPUs.

## Slide 135: 2.3.4 Evolution of the performance of integrated graphics in the Core 2 line (3)
Graphics performance increase in subsequent Core generations, as revealed
by Intel [24]
Skylake (2018)
Broadwell (2015)
Haswell (2013)
Ivy Bridge (2012)
Sandy Bridge (2011)

## Slide 136: 2.3.4 Evolution of the performance of integrated graphics in the Core 2 line (4)
Remark to Intel’s performance data stated in the previous Figure
In the preceding Figure Intel reports a more than 100-fold improvement in
graphics performance achieved with its 6th generation (Skylake) processors.
Nevertheless, this statement has to be taken with certain caution since the
reference point of this performance improvement is Intel’s first or second gen.
graphics (not specified) implemented yet in the NB from about 1998.
If we take into account the graphics performance figures given for the integrated
graphics implementations (in the 6th gen. Core processors vs. the 2nd gen. Core
processors) we get a real improvement of about 140/25=5,6.
This value is pretty much the same value as the ratio of the EUs of the 6th and
2nd generation Core 2 processors: 72/12=6.

## Slide 137: 2.3 Evolution of key features of integrated graphics in Intel’s client processors (1)
For their Core 2 processors Intel developed two GPU families:
the HD family and
the Xe family.
The HD family of GPUs was introduced along with the Westmere line, including
Intel’s first integrated, albeit still in package integrated graphics, in 2010.
Overview of Intel’s graphics families
Mobile processors, and client processors for laptops and general purpose desktops
usually include integrated GPUs whereas desktop processors designed for gaming
typically have only discrete graphics and do not include integrated GPUs.
Similarly, HEDTs and servers do not need integrated GPUs.
Summing up the evolution of key features of integrated graphics in Intel’s Core 2-based
client processors -1

## Slide 138: 2.3 Evolution of key features of integrated graphics in Intel’s client processors (2)
Next the GPU became integrated onto the processor die in the 2nd gen. Sandy Bridge
line in 2011.
Intel implemented HD graphics with continuous enhancements for all of their processors
manufactured up to (and including) the 14 nm technology, at last in the Comet Lake line
(2019), however lastly, it was renamed to UHD graphics, as the following Tables indicate.
a) Intel’s HD graphics family -1
The HD family of GPUs was introduced along with the Westmere line in 2010,
nevertheless it was still in package integrated graphics including separate CPU
and graphics dies, enclosed into a package.
Summing up the evolution of key features of integrated graphics in Intel’s Core 2-based
client processors -2
b) Intel’s Xe graphics family
The Xe family of GPUs is a complete re-design targeting all major market segments
from client processors used for gaming up to data centers with HPC workloads.
In client processors Xe graphics appeared along with the 10 nm processors, first
in Intel’s 10th generation Ice Lake line in 2019, named as the 11th gen. Iris Xe graphics,
as indicated in the next Table.

## Slide 139: 2.3 Evolution of key features of integrated graphics in Intel’s client processors (3)
Designation of Intel’s graphics generations
Intel’s microarchitectures and graphics generations are designated differently,
for example, Intel’s first on-die integrated graphics was implemented in the
2nd gen. Sandy Bridge line in 2011 and became Intel’s 6th gen. HD graphics, (as indicated
in the previous Table).
Summing up the evolution of key features of integrated graphics in Intel’s Core 2-based
client processors -3

## Slide 140: 2.3 Evolution of key features of integrated graphics in Intel’s client processors (4)
Case example: The 12th gen. Xe LP GPU of 11th gen. Tiger Lake processors
Summing up the evolution of key features of integrated graphics in Intel’s Core 2-based
client processors -4
Intel’s 12th gen. Xe LP EUs are built up of modules where each module includes
dual subslices with shared thread control [23].
Subslices are subunits of slices including among others 16 EUs (Execution Units)
for performing FX/FP computations.
There are different numbers of subslices in Intel’s 12th gen. graphics implementations,
e.g. 6 in 12th gen. Xe LP GPUs.
Consequently, 12th gen. Xe LP GPUs may include up to 96 EUs.

## Slide 141: 2.3 Evolution of key features of integrated graphics in Intel’s client processors (5)
Layout of 12th gen. graphics EUs of Tiger Lake processors [22]
On the IP 0 there are two 8-wide (8x32-bit)
SIMD ALUs (an FP and an FX ALU) available,
they operate exclusively and can perform up to
whereas on the IP 1 there is an
Extended Math (EM) unit available,
that can perform up to two
Extended Math (EM) operations
(to calculate trigonometric functions etc.)
8 FP32, 16 FP16 FMA operations or
8 FX32, 16 FX16, 32 FX8 FMA operations,
Summing up the evolution of key features of integrated graphics in Intel’s Core 2-based
client processors -5

## Slide 142: 2.3 Evolution of key features of integrated graphics in Intel’s client processors (6)
Summing up the evolution of key features of integrated graphics in Intel’s Core 2-based
client processors -6
Raising the max. number of graphics EUs in GPUs of Core 2 processors
Intel raised the max number of graphics EUs in their GPUs immensely, from 12
(in the Sandy Bridge) to 96 (in the Tiger Lake) in less than 10 years, this means
roughly a 10-fold increase in 10 years.
The graphics performance is expected to scale more or less linearly with the
number of EUs provided in the GPU.
Raising the max. number of graphics EUs in GPUs of Core 2 processors

## Slide 143
3. Evolution of HEDT (High-End Desktop) processors
Notes: 143

## Slide 144: 3. Evolution of HEDT (High-End Desktop) processors (1)
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smarphones
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smartphones
Desktops
Servers
Recent major processor categories of Intel
Xeon E7/E5/E3
Platinum/Gold etc.
Clients
(Desktops/Laptops)
Core i9/i7/i5/i3
(Basic architectures)
HEDTs
(High-End Desktops)
Core i7/i9
(Extreme Edition
or X models)
3. Evolution of HEDT (High-End DeskTop) processors
Mobiles
(Tablets, Smartphones)
Atom lines
Atom lines
(+ LP Core models)

## Slide 145: 3. Evolution of HEDT (High-End Desktop) processors (2)
HEDTs (High-End DeskTops)
HEDTs aim at graphics enthusiasts, hardcore gamers and multimedia content creators.

## Slide 146: 3. Evolution of HEDT (High-End Desktop) processors (3)
Hardcore gamer scenario [25]

## Slide 147: 3. Evolution of HEDT (High-End Desktop) processors (4)
1. Introduction -1
More PCIe lanes
To attach up to 4 graphics cards by 8 or 16 PCIe lanes per card, HEDT processors
need at least 4x8=32 PCIe lanes vs. 16 lanes typically provided by DT processors.
The next Tables show actual numbers of PCIe lanes implemented in
Core 2-based HEDT lines.
What are the main requirements for HEDT processors compared to DT processors?

## Slide 148: 3. Evolution of HEDT (High-End Desktop) processors (5)
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachm. | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Core 2 Extreme X6800 | 65 nm | 7/2006 | 2C | Via MCH | DDR3-1066 | 32 PCIe 2.0 on the X38 | 2 | X38 | 65 W | LGA 775
Core 2 Extreme QX 6xxx | 65 nm | 11/2006 | 2x2C |  |  |  |  |  | 130 W | LGA 775
 |  |  |  |  |  |  |  |  | 130 W | LGA 775
Core 2 Extreme QX 9650 (Penryn) | 45 nm | 11/2007 | 2x2C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 32 PCIe 2.0 on the X48 | 2 | X48 | 136 W | LGA 775
Core 2 Extreme QX 9770 (Penryn) | 45 nm | 3/2008 | 2x2C |  |  |  |  |  |  | 
1. G. Nehalem EE | 45 nm | 11/2008 | 4C | On-die MC | DDR3-1067 | 36 PCIe 2.0 on the X58 | 3 | X58 (Tylersburg) | 130 W | LGA 1366
Westmere EE | 32 nm | 3/2010 | 6C |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 130 W | LGA 1366
Sandy Bridge E | 32 nm | 11/2011 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 40 PCIe 2.0 on-die | 4 | X79 (Patsburg) | 130 W/ 150 W | LGA 2011
Ivy Bridge E | 22 nm | 9/2013 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1866 | 40 PCIe 3.0 on-die | 4 |  | 130 W | LGA 2011
Haswell E | 14 nm | 8/2014 | 8C |  | DDR4-2133 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Broadwell E | 14 nm | 5/2016 | 10C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2400 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Skylake X | 14 nm | 6/2017 | 18C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 140 W | LGA 2066
(Kaby Lake X) | 14 nm | 6/2017 | 4C |  | DDR4-2666 | 16 PCIe 3.0 on-die | 4 | X299 (Basin Falls) | 112 W | LGA 2066
Number of PCIe lanes in Core 2-based HEDT processors -1

## Slide 149: 3. Evolution of HEDT (High-End Desktop) processors (6)
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachment | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Skylake-X Refresh | 14 nm | 11/2018 | 18C | On-die MC | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 165 W | LGA- 2066
Cascade Lake-X (Server arch.) | 14 nm | 11/2019 | 18C |  | DDR4-2933 | 48 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 165 W | LGA 066
Number of PCIe lanes in Core 2-based HEDT processors -2
In the course of the evolution of the Core 2 family, HEDT processors provide
more and more PCIe lanes.
As long as early HEDT processors provided 32 (PCIe 2.0) lanes, recent HEDT processors
offer up to 48 (PCIe 3.0) lanes, as seen in the preceding Tables and indicated in the
next Figure.

## Slide 150: 3. Evolution of HEDT (High-End Desktop) processors (7)
DT processors: 16 lanes
(1x16 or 2x8 or 1x8+2x4)
PCIe lanes provided on the processor die
HEDT processors: 40+ lanes (typical)
(configurable, e.g. 2x x16 + 1x x8 or 4x x8)
PCIe 3.0 lanes
PCIe 2.0 lanes
PCIe generation
Mem.
P
Periph. Contr.
PCIe
2.0
x16/
2x x8
x16/
2x x8
Mem.
P
Periph. Contr.
PCIe
3.0
Intel 2. gen. Nehalem (Lynnfield) (4C), 2 MCh
with P55 (2009)
Intel Sandy Bridge (4C), 2 MCh with P67 (2011)
P55/P67
Z77/Z87/Z97/
Z170
Intel Ivy Bridge-E (6C), 4 MCh with X79 (2013)
PCIe lanes and memory channels on Core 2-based DT and HEDT processors
PCIe
3.0
40-48
configurable
lanes
Mem.
P
Periph. Contr.
X79/Z99/
X299
PCIe
2.0
40
configurable
lanes
Mem.
P
Periph. Contr.
X79
Intel Sandy Bridge-E (6C), 4 MCh with X79 (2011)
Intel Ivy Bridge (4C), 2 MCh with Z77 PCH (2012)
Intel Haswell (4C), 2 MCh with Z87 PCH (2013)
Intel Broadwell (4C), 2 MCh with Z97 PCH (2015)
Intel Skylake-S (4C), 2 MCh with Z170 PCH (2015)
and subsequent lines
40 lanes beginning with
44 lanes beginning with
Intel Skylake-X (18C), 4 MCh with X299 (2017)
48 lanes beginning with
Intel Cascade Lake-X (18C), 4 MCh with X279 (2019)

## Slide 151: 3. Evolution of HEDT (High-End Desktop) processors (8)
b) More cores
Graphics programs operate mostly on pixels, permitting massively parallel execution,
consequently HEDT processors should have as many cores as feasible by the
available technology.
Accordingly, while IC technology has advanced, core counts of HEDTs rose from
2 to 18 until now (02/2022).

## Slide 152: 3. Evolution of HEDT (High-End Desktop) processors (9)
Core counts -1
The above HEDT models and lines are unlocked.
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachm. | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Core 2 Extreme X6800 | 65 nm | 7/2006 | 2C | Via MCH | DDR3-1066 | 32 PCIe 2.0 on the X38 | 2 | X38 | 65 W | LGA 775
Core 2 Extreme QX 6xxx | 65 nm | 11/2006 | 2x2C |  |  |  |  |  | 130 W | LGA 775
 |  |  |  |  |  |  |  |  | 130 W | LGA 775
Core 2 Extreme QX 9650 (Penryn) | 45 nm | 11/2007 | 2x2C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 32 PCIe 2.0 on the X48 | 2 | X48 | 136 W | LGA 775
Core 2 Extreme QX 9770 (Penryn) | 45 nm | 3/2008 | 2x2C |  |  |  |  |  |  | 
1. G. Nehalem EE | 45 nm | 11/2008 | 4C | On-die MC | DDR3-1067 | 36 PCIe 2.0 on the X58 | 3 | X58 (Tylersburg) | 130 W | LGA 1366
Westmere EE | 32 nm | 3/2010 | 6C |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 130 W | LGA 1366
Sandy Bridge E | 32 nm | 11/2011 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 40 PCIe 2.0 on-die | 4 | X79 (Patsburg) | 130 W/ 150 W | LGA 2011
Ivy Bridge E | 22 nm | 9/2013 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1866 | 40 PCIe 3.0 on-die | 4 |  | 130 W | LGA 2011
Haswell E | 14 nm | 8/2014 | 8C |  | DDR4-2133 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Broadwell E | 14 nm | 5/2016 | 10C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2400 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Skylake X | 14 nm | 6/2017 | 18C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 140 W | LGA 2066
(Kaby Lake X) | 14 nm | 6/2017 | 4C |  | DDR4-2666 | 16 PCIe 3.0 on-die | 4 | X299 (Basin Falls) | 112 W | LGA 2066

## Slide 153: 3. Evolution of HEDT (High-End Desktop) processors (10)
Core counts -2
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachment | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Skylake-X Refresh | 14 nm | 11/2018 | 18C | On-die MC | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 165 W | LGA- 2066
Cascade Lake-X (Server arch.) | 14 nm | 11/2019 | 18C |  | DDR4-2933 | 48 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 165 W | LGA 066

## Slide 154: 3. Evolution of HEDT (High-End Desktop) processors (11)
Remark
The Kaby Lake-X models in fact do not fit into the traditional HEDT lines, they are
actually the highest performance models of the Kaby Lake line and are designated
as mobile models.

## Slide 155: 3. Evolution of HEDT (High-End Desktop) processors (12)
2006
2003
2010
2014
2016
2006
Evolution of the core counts in Intel's HEDT lines (Based on [26])
2017
Core 2
Extreme
X6800
Westmere EE
Haswell E
Broadwell E
Core 2
Extreme
QX6700
Skylake X
18
18 CORE
Number of cores
Pentium 4 EE
3.2

## Slide 156: 3. Evolution of HEDT (High-End Desktop) processors (13)
c) More memory channels
To provide enough bandwidth for a higher number of cores than implemented
in DTs, HEDT processors are typically designed with more memory channels than
available in DTs.
In fact, after core counts rose to 6, Intel raised also the number of memory
channels to four and held on this figure until now.

## Slide 157: 3. Evolution of HEDT (High-End Desktop) processors (14)
Number of memory channels -1
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachm. | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Core 2 Extreme X6800 | 65 nm | 7/2006 | 2C | Via MCH | DDR3-1066 | 32 PCIe 2.0 on the X38 | 2 | X38 | 65 W | LGA 775
Core 2 Extreme QX 6xxx | 65 nm | 11/2006 | 2x2C |  |  |  |  |  | 130 W | LGA 775
 |  |  |  |  |  |  |  |  | 130 W | LGA 775
Core 2 Extreme QX 9650 (Penryn) | 45 nm | 11/2007 | 2x2C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 32 PCIe 2.0 on the X48 | 2 | X48 | 136 W | LGA 775
Core 2 Extreme QX 9770 (Penryn) | 45 nm | 3/2008 | 2x2C |  |  |  |  |  |  | 
1. G. Nehalem EE | 45 nm | 11/2008 | 4C | On-die MC | DDR3-1067 | 36 PCIe 2.0 on the X58 | 3 | X58 (Tylersburg) | 130 W | LGA 1366
Westmere EE | 32 nm | 3/2010 | 6C |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 130 W | LGA 1366
Sandy Bridge E | 32 nm | 11/2011 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 40 PCIe 2.0 on-die | 4 | X79 (Patsburg) | 130 W/ 150 W | LGA 2011
Ivy Bridge E | 22 nm | 9/2013 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1866 | 40 PCIe 3.0 on-die | 4 |  | 130 W | LGA 2011
Haswell E | 14 nm | 8/2014 | 8C |  | DDR4-2133 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Broadwell E | 14 nm | 5/2016 | 10C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2400 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Skylake X | 14 nm | 6/2017 | 18C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 140 W | LGA 2066
(Kaby Lake X) | 14 nm | 6/2017 | 4C |  | DDR4-2666 | 16 PCIe 3.0 on-die | 4 | X299 (Basin Falls) | 112 W | LGA 2066

## Slide 158: 3. Evolution of HEDT (High-End Desktop) processors (15)
Number of memory channels -2
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachment | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Skylake-X Refresh | 14 nm | 11/2018 | 18C | On-die MC | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 165 W | LGA- 2066
Cascade Lake-X (Server arch.) | 14 nm | 11/2019 | 18C |  | DDR4-2933 | 48 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 165 W | LGA 066

## Slide 159: 3. Evolution of HEDT (High-End Desktop) processors (16)
d) Lack of integrated graphics
HEDTs do not provide integrated graphics, as they make use of one or more
high-performance discrete graphics cards that supersede the additional
use of less performant integrated graphics.

## Slide 160: 3. Evolution of HEDT (High-End Desktop) processors (17)
e) Unlocked clock multiplier
Intel’s HEDT processors are typically unlocked, meaning that the clock multiplier
isn’t fixed, i.e. it is variable to allow overclocking.
(The clock multiplier is a circuit that generates the clock frequency by
multiplying the bus frequency (100/133 MHz) by an integer delivered by
the PCU (Power Control Unit).

## Slide 161: 3. Evolution of HEDT (High-End Desktop) processors (18)
f) Higher TDP
Clearly, more PCIe lanes, more cores, memory channels etc. need more power,
so HEDT processors typically have 130 to 165 W power consumption vs. 65 to
95 W, usually consumed by DT processors, as the Tables below indicate.

## Slide 162: 3. Evolution of HEDT (High-End Desktop) processors (19)
TDP (Thermal Design Power) values of Core 2-based HEDT models-1
TDP: Serves as the reference value for designing the cooling system.
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachm. | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Core 2 Extreme X6800 | 65 nm | 7/2006 | 2C | Via MCH | DDR3-1066 | 32 PCIe 2.0 on the X38 | 2 | X38 | 65 W | LGA 775
Core 2 Extreme QX 6xxx | 65 nm | 11/2006 | 2x2C |  |  |  |  |  | 130 W | LGA 775
 |  |  |  |  |  |  |  |  | 130 W | LGA 775
Core 2 Extreme QX 9650 (Penryn) | 45 nm | 11/2007 | 2x2C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 32 PCIe 2.0 on the X48 | 2 | X48 | 136 W | LGA 775
Core 2 Extreme QX 9770 (Penryn) | 45 nm | 3/2008 | 2x2C |  |  |  |  |  |  | 
1. G. Nehalem EE | 45 nm | 11/2008 | 4C | On-die MC | DDR3-1067 | 36 PCIe 2.0 on the X58 | 3 | X58 (Tylersburg) | 130 W | LGA 1366
Westmere EE | 32 nm | 3/2010 | 6C |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 130 W | LGA 1366
Sandy Bridge E | 32 nm | 11/2011 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1600 | 40 PCIe 2.0 on-die | 4 | X79 (Patsburg) | 130 W/ 150 W | LGA 2011
Ivy Bridge E | 22 nm | 9/2013 | 6C |  |  |  |  |  |  | 
 |  |  |  |  | DDR3-1866 | 40 PCIe 3.0 on-die | 4 |  | 130 W | LGA 2011
Haswell E | 14 nm | 8/2014 | 8C |  | DDR4-2133 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Broadwell E | 14 nm | 5/2016 | 10C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2400 |  | 4 | X99 (Wellsburg) | 140 W | LGA 2011-3
Skylake X | 14 nm | 6/2017 | 18C |  |  |  |  |  |  | 
 |  |  |  |  | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 140 W | LGA 2066
(Kaby Lake X) | 14 nm | 6/2017 | 4C |  | DDR4-2666 | 16 PCIe 3.0 on-die | 4 | X299 (Basin Falls) | 112 W | LGA 2066

## Slide 163: 3. Evolution of HEDT (High-End Desktop) processors (20)
TDP (Thermal Design Power) values of Core 2-based HEDT models -2
Processor | Techn. | Date of intro. | No. of cores up to | Memory attachment | Mem. speed up to | PCIe lanes | No. of mem. channels | MCH | TDP | Processor socket
Skylake-X Refresh | 14 nm | 11/2018 | 18C | On-die MC | DDR4-2666 | 44 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 165 W | LGA- 2066
Cascade Lake-X (Server arch.) | 14 nm | 11/2019 | 18C |  | DDR4-2933 | 48 PCI-3.0 on-die | 4 | X299 (Basin Falls) | 165 W | LGA 066

## Slide 164: 3. Evolution of HEDT (High-End Desktop) processors (21)
Summing up key issues of HEDT (High-End DeskTop) processors -1
More PCIe lanes
What are the main requirements for HEDT processors vs. DT processors?
b) More cores
c) More memory channels
HEDTs aim at graphics enthusiasts, hardcore gamers and multimedia content creators.
To attach up to 4 graphics cards by 8 or 16 PCIe lanes per card, HEDT processors
need at least 4x8=32 PCIe lanes vs. 16 lanes typically provided by DT processors.
In the course of the evolution of the Core 2 family, HEDT processors provide
more and more PCIe lanes; as long as early HEDT processors provided
32 (PCIe 2.0) lanes, recent HEDT processors offer up to 48 (PCIe 3.0) lanes.
Graphics programs operate mostly on pixels, permitting massively parallel execution,
consequently HEDT processors should have as many cores as feasible by the
available technology.
Accordingly, while IC technology has advanced, core counts of HEDTs rose from 2 to 18 until now (02/2022).
To provide enough bandwidth for a higher number of cores than implemented
in DTs, HEDT processors are typically designed with more memory channels than
available in DTs.
In fact, after core counts rose to 6, Intel raised also the number of memory
channels to four and held on this figure until now.

## Slide 165: 3. Evolution of HEDT (High-End Desktop) processors (22)
d) Lack of integrated graphics
e) Unlocked clock multiplier
f) Higher TDP
Summing up key issues of HEDT (High-End DeskTop) processors -2
HEDTs do not provide integrated graphics, as they make use of one or more
high performance discrete graphics cards that supersede the additional
use of less performant integrated graphics.
Intel’s HEDT processors are typically unlocked, meaning that the clock multiplier
isn’t fixed, i.e. it is variable to allow overclocking.
(The clock multiplier is a circuit that generates the clock frequency by
multiplying the bus frequency (100/133 MHz) by an integer delivered by
the PCU (Power Control Unit).
Clearly, more PCIe lanes, more cores, memory channels etc. need more power,
so HEDT processors typically have 130 to 165 W power consumption vs. 65 to
95 W, usually consumed by DT processors, as the Tables below indicate.

## Slide 166
4. Evolution of high-end 2S server processors
Notes: 166

## Slide 167: 4. Evolution of high-end 2S server processors (1)
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smarphones
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smartphones
Desktops
Servers
Recent major processor categories of Intel
Xeon E7/E5/E3
Platinum/Gold etc.
Clients
(Desktops/Laptops)
Core i9/i7/i5/i3
(Basic architectures)
HEDTs
(High-End Desktops)
Core i7/i9
(Extreme Edition
or X models)
4. Evolution of high-end 2S server processors
Mobiles
(Tablets/Smartphones)
Atom lines
Atom lines
(+ LP Core models)

## Slide 168: 4. Evolution of high-end 2S server processors (2)
Server platforms classified according to the number of processors supported
2S (DP)
server platforms
Server platforms
Platforms for more than 8 sockets
2- processor server platforms
(2-socket server platforms)
4S/8S (MP)
server platforms
4/8-processor server platforms
(4/8-socket server platforms)
Server platforms for
more than the Intel
supported number of
sockets
(4 or 8 sockets)
They need third party
node controllers
Uniprocessor server platforms
(UP-server platforms)
1-processor server platforms
(1-socket server platforms)
Multiprocessor server platforms
Server platforms supporting more than one processor
(Multi-socket server platforms)
S: Socket
DP: Dual Processor
MP: Multi-Processor
This Section is concerned only with 2S server processors due to their dominance
in servers, as indicated in the next Figure.

## Slide 169: 4. Evolution of high-end 2S server processors (3)
Recent market share of 1S and 2S servers [27]
Recently, 2S servers dominate by far the server market (by about 80%).

## Slide 170: 4. Evolution of high-end 2S server processors (4)
Platform4 | Core | Techn. | Intro. | High performance Core 2-based multicore 2S server processors | Core count up to | Trans. count [106/109] | Die size [mm2]
 | Pentium 4 Prescott DP | 90 nm | 6/2004 | Xeon DP 90 nm (Nocona) | 1C | 125 | 112
 | Pentium 4 Prescott 2M DP | 90 nm | 10/2005 | Xeon DP 2008 (Paxville DP) | 2x1C | 2x169 | 2x135
Bensley | Pentium 4 Prescott 2M DP | 65 nm | 5/2006 | Xeon 5000 (Dempsey) | 2x1C | 2x188 | 2x81
 | Core2 | 65 nm | 6/2006 | Xeon 5100 (Woodcrest) | 2C | 291 | 143
 | Core2 | 65 nm | 11/2006 | Xeon 5300 (Clovertown) | 2x2C | 2x291 | 2x143
 | Penryn | 45 nm | 11/2007 | Xeon 5400 (Harpertown) | 2x2C | 2x410 | 2x107
Boxboro-EX | Nehalem | 45 nm | 3/2010 | Xeon X6500 (Beckton/Nehalem-EX) | 8C | 2.3 | 513
 | Westmere | 32 nm | 4/2011 | Xeon E7-28xx (Westmere-EX) | 10C | 2.6 | 512
Brickland | Ivy Bridge | 22 nm | 2/2014 | Xeon E7-28xx v2 (Ivy Bridge-EX) | 15C | 4.31 | 541
 | Haswell | 22 nm | 9/2014 | Xeon E5-2600xx v3 (Haswell-EP) | 18C | 5.69 | 662
 | Broadwell | 14 nm | 4/2016 | Xeon E5-26xx v4 (Broadwell-EP) | 22C | 7.2 | 456
Purley | Skylake | 14 nm | 7/2017 | Xeon Platinum 8176/80 (Skylake-SP) | 28C | 8.0? | ~694
 | Cascade Lake | 14 nm | 4/2019 | Xeon Platinum 8276/80 (Cascade Lake-SP) | 28C | n.a. | n.a.
 | Cascade Lake | 14 nm | 4/2019 | Xeon Platinum 9282 (Cascade Lake-AP) | 2x28C | n.a. | n.a.
 | Cascade Lake R | 14 nm | 2/2020 | Xeon Gold 6238R/6258 (Cascade Lake R) | 28C | n.a. | n.a.
Whitney | Ice Lake | 10 nm | 4/2020 | Xeon Platinum 8380 (Ice Lake-SP) | 40C | n.a. | ≈640
Key features of Intel’s 64-bit x86-based HE 2S server processor dies – Overview -1

## Slide 171: 4. Evolution of high-end 2S server processors (5)
Die area and transistor count of Intel’s 2S server processors
Although Intel stopped releasing die area and transistor count data, previous figures
indicate that
recent high-end 2S server processors might have a die area of 600-700 mm2
and include much more than 10 billion transistors,
as the next Table shows.

## Slide 172: 4. Evolution of high-end 2S server processors (6)
Platform4 | Core | Techn. | Intro. | High performance Core 2-based multicore 2S server processors | Core count up to | Trans. count [106/109] | Die size [mm2]
 | Pentium 4 Prescott DP | 90 nm | 6/2004 | Xeon DP 90 nm (Nocona) | 1C | 125 | 112
 | Pentium 4 Prescott 2M DP | 90 nm | 10/2005 | Xeon DP 2008 (Paxville DP) | 2x1C | 2x169 | 2x135
Bensley | Pentium 4 Prescott 2M DP | 65 nm | 5/2006 | Xeon 5000 (Dempsey) | 2x1C | 2x188 | 2x81
 | Core2 | 65 nm | 6/2006 | Xeon 5100 (Woodcrest) | 2C | 291 | 143
 | Core2 | 65 nm | 11/2006 | Xeon 5300 (Clovertown) | 2x2C | 2x291 | 2x143
 | Penryn | 45 nm | 11/2007 | Xeon 5400 (Harpertown) | 2x2C | 2x410 | 2x107
Boxboro-EX | Nehalem | 45 nm | 3/2010 | Xeon X6500 (Beckton/Nehalem-EX) | 8C | 2.3 | 513
 | Westmere | 32 nm | 4/2011 | Xeon E7-28xx (Westmere-EX) | 10C | 2.6 | 512
Brickland | Ivy Bridge | 22 nm | 2/2014 | Xeon E7-28xx v2 (Ivy Bridge-EX) | 15C | 4.31 | 541
 | Haswell | 22 nm | 9/2014 | Xeon E5-2600xx v3 (Haswell-EP) | 18C | 5.69 | 662
 | Broadwell | 14 nm | 4/2016 | Xeon E5-26xx v4 (Broadwell-EP) | 22C | 7.2 | 456
Purley | Skylake | 14 nm | 7/2017 | Xeon Platinum 8176/80 (Skylake-SP) | 28C | 8.0? | ~694
 | Cascade Lake | 14 nm | 4/2019 | Xeon Platinum 8276/80 (Cascade Lake-SP) | 28C | n.a. | n.a.
 | Cascade Lake | 14 nm | 4/2019 | Xeon Platinum 9282 (Cascade Lake-AP) | 2x28C | n.a. | n.a.
 | Cascade Lake R | 14 nm | 2/2020 | Xeon Gold 6238R/6258 (Cascade Lake R) | 28C | n.a. | n.a.
Whitney | Ice Lake | 10 nm | 4/2020 | Xeon Platinum 8380 (Ice Lake-SP) | 40C | n.a. | ≈640
Key features of Intel’s 64-bit x86-based HE 2S server processor dies – Overview -2

## Slide 173: 4. Evolution of high-end 2S server processors (7)
The key challenge in designing memory subsystems of server processors
The key challenge in designing memory subsystems of server processors becomes
obvious when we contrast the grows rates of core counts and memory speeds
achieved over generations.
Let’ first consider the rate of rising core counts.

## Slide 174: 4. Evolution of high-end 2S server processors (8)
Platform440c40C4 | Core | Techn. | Intro. | High performance Core 2-based multicore 2S server processors | Core count up to | Trans. count [106/109] | Die size [mm2]
 | Pentium 4 Prescott DP | 90 nm | 6/2004 | Xeon DP 90 nm (Nocona) | 1C | 125 | 112
 | Pentium 4 Prescott 2M DP | 90 nm | 10/2005 | Xeon DP 2008 (Paxville DP) | 2x1C | 2x169 | 2x135
Bensley | Pentium 4 Prescott 2M DP | 65 nm | 5/2006 | Xeon 5000 (Dempsey) | 2x1C | 2x188 | 2x81
 | Core2 | 65 nm | 6/2006 | Xeon 5100 (Woodcrest) | 2C | 291 | 143
 | Core2 | 65 nm | 11/2006 | Xeon 5300 (Clovertown) | 2x2C | 2x291 | 2x143
 | Penryn | 45 nm | 11/2007 | Xeon 5400 (Harpertown) | 2x2C | 2x410 | 2x107
Boxboro-EX | Nehalem | 45 nm | 3/2010 | Xeon X6500 (Beckton/Nehalem-EX) | 8C | 2.3 | 513
 | Westmere | 32 nm | 4/2011 | Xeon E7-28xx (Westmere-EX) | 10C | 2.6 | 512
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-28xx v2 (Ivy Bridge-EX) | 15C | 4.31 | 541
 | Haswell | 22 nm | 9/2014 | E5-2600xx v3 (Haswell-EP) | 18C | 5.69 | 662
 | Broadwell | 14 nm | 4/2016 | E5-26xx v4 (Broadwell-EP) | 22C | 7.2 | 456
Purley | Skylake | 14 nm | 7/2017 | Xeon Platinum 8176/80 | 28C | 8.0? | ~694?
 | Cascade Lake | 14 nm | 4/2019 | Xeon Platinum 8276/8280 | 28C | n.a. | n.a.
 | Cascade Lake-AP | 14 nm | 4/2019 | Xeon Platinum 9282 | 2x28C | n.a. | n.a.
 | Cascade Lake R | 14 nm | 2/2020 | Xeon Gold 6238R/6258R | 28C | n.a. | n.a.
Whitley | Ice Lake | 10 nm | 4/2021 | Xeon Platinum 8380 | 40C | n.a. | ≈640
Evolution of core counts in Intel's 64-bit x86-based high-end 2S server processors

## Slide 175: 4. Evolution of high-end 2S server processors (9)
Remark to Intel’s 56-core Cascade Lake 9200-AP processor line
With this processor line Intel intends to encounter AMD’s 64-core EPYC Rome line.
The 9200-AP is a dual-chip module with the Cascade Lake-SP dies interconnected
properly, presumable by an UPI bus, and placed into a BGA (Ball Grid Array)
package, as indicated in the left Figure, that will be surface mounted (soldered)
onto the mainboard.
Figure: Dual-chip module of
the 9200-AP [28]
Dual-socket server
based on the 9200-AP [28]
A dual socket server built up of the Cascade Lake 9200-AP (see the Figure on the
right) appears and operates actually as a 4-processor server.

## Slide 176: 4. Evolution of high-end 2S server processors (9b)
Rising core counts in Intel’s high-end Core 2-based 2S server processors -1
Core count
2006
2008
2010
2012
2014
2016
Year
Nehalem-EX
(45 nm)
Westmere-EX
(32 nm)
Ivy-Bridge-EX
(22 nm)
Broadwell-EP
(14 nm)
*
*
*
*
*
2
4
8
18
28
24
10
6
15
*
*
~2x/4 years
Emergence of
L3 caches in Core 2-based
high-end 2S processor lines
*
Haswell-EP
(22 nm)
12
2018
56
*
Cascade Lake-AP
(Two dies)
(14 nm)
2020
40
*
*
Skylake-SP
Platinum/Gold
(14 nm)
*
Cascade Lake-SP
Platinum/Gold
(14 nm)
Ice Lake-SP
(10 nm)
~2x/2 years
*
5100
(Core 2-based)
(65 nm)
Two-die
implementations
5400
(Penryn b.)
(45 nm)
5300
(Core 2 b.)
(65 nm)
DP 2.8 GHz
(Pentium 4 b.)
(90 nm)
b.: based

## Slide 177: 4. Evolution of high-end 2S server processors (9c)
Intel rose the core count in their 2S server processors at two different rates,
as follows:
Rising core counts in Intel’s high-end Core 2-based 2S server processors -2
As the previous graph shows,

## Slide 178: 4. Evolution of high-end 2S server processors (10)
Doubling core counts in L3-less high-end Core 2-based 2S server processors
about biannually -1
Core count
2006
2008
2010
2012
2014
2016
Year
Nehalem-EX
(45 nm)
Westmere-EX
(32 nm)
Ivy-Bridge-EX
(22 nm)
Broadwell-EP
(14 nm)
*
*
*
*
*
2
4
8
18
28
24
10
6
15
*
*
~2x/4 years
Emergence of
L3 caches in Core 2-based
high-end 2S processor lines
*
Haswell-EP
(22 nm)
12
2018
56
*
Cascade Lake-AP
(Two dies)
(14 nm)
2020
40
*
*
Skylake-SP
Platinum/Gold
(14 nm)
*
Cascade Lake-SP
Platinum/Gold
(14 nm)
Ice Lake-SP
(10 nm)
~2x/2 years
*
5100
(Core 2-based)
(65 nm)
Two-die
implementations
5400
(Penryn b.)
(45 nm)
5300
(Core 2 b.)
(65 nm)
DP 2.8 GHz
(Pentium 4 b.)
(90 nm)

## Slide 179: 4. Evolution of high-end 2S server processors (11)
Doubling core counts in early, L3-less high-end Core 2-based 2S server processors about biannually -2
Doubling core counts in the first phase of the evolution roughly biannually is quite
evident in the light of Moore’s rule, since the evolution of IC technology allowed
doubling transistor counts and consequently core counts as well, roughly every
two years.
This evolution however ended when L3 caches appeared and occupied large parts
of the silicon area.

## Slide 180: 4. Evolution of high-end 2S server processors (12)
Core count
2006
2008
2010
2012
2014
2016
Year
Nehalem-EX
(45 nm)
Westmere-EX
(32 nm)
Ivy-Bridge-EX
(22 nm)
Broadwell-EP
(14 nm)
*
*
*
*
*
2
4
8
18
28
24
10
6
15
*
*
~2x/4 years
Emergence of
L3 caches in Core 2-based
high-end 2S processor lines
*
Haswell-EP
(22 nm)
12
2018
56
*
Cascade Lake-AP
(Two dies)
(14 nm)
2020
40
*
*
Skylake-SP
Platinum/Gold
(14 nm)
*
Cascade Lake-SP
Platinum/Gold
(14 nm)
Ice Lake-SP
(10 nm)
~2x/2 years
*
5100
(Core 2-based)
(65 nm)
Two-die
implementations
5400
(Penryn b.)
(45 nm)
5300
(Core 2 b.)
(65 nm)
DP 2.8 GHz
(Pentium 4 b.)
(90 nm)
b) Slowing down the growth rate of core counts in high-end 2S server processors
after L3 caches emerged -1

## Slide 181: 4. Evolution of high-end 2S server processors (13)
Concerning this, we point out that after L3 caches arrived, transistor counts
in Core 2-based 4S server processors has been raised at a similar rate
i.e. (doubled in about 4 years), as the Table below and the subsequent Figure
indicate.
Family | Technology | Introduced | Core count | L3 cache | Transistors (million) | Die area (mm2)
7300 (Tigerton) | 65 nm | 9/2007 | 2x2 | no L3 | 582 | 286
7400 (Dunnington) | 45 nm | 9/2008 | 6 | 16 MB | 1900 | 503
Nehalem-EX | 45 nm | 3/2010 | 8 | 8x3 MB | 2300 | 513
Westmere-EX | 32 nm | 4/2011 | 10 | 10x3 MB | 2600 | 512
Ivy Bridge-EX | 22 nm | 2/2014 | 15 | 14x2.5 MB | 4310 | 541
Haswell-EX | 22 nm | 5/2015 | 18 | 18x2.5 MB | 5700 | 662
Broadwell-EX | 14 nm | 6(2016 | 24 | 24x2.5 MB | 7200 | 456
(Source: Intel data)
Table: Implementation data of Intel’s Core 2 based high-end 4S server processors
b) Slowing down the growth rate of core counts in high-end 2S server processors
after L3 caches emerged -2
As seen in the previous Figure, after L3 caches emerged, the evolution of core counts
slowed down to a rate of doubling approximately every four years.

## Slide 182: 4. Evolution of high-end 2S server processors (14)
Transistor count
(billion)
2006
2008
2010
2012
2014
2016
Year
7400
(45 nm)
Nehalem-EX
(45 nm)
Westmere-EX
(32 nm)
Ivy-Bridge-EX
(22 nm)
Broadwell-EX
(14 nm)
*
*
*
2
4
8
10
6
*
*
~2x/4 years
Emergence of
L3 caches
in the Core 2 line
*
Haswell-EX
(22 nm)
Growth rate of transistor counts in Core 2-based high-end 4S server processors
The reason why transistor counts rose slower than predicted by Moore’s law is the
power budget limitation of the die.
At the same time this is also the reason why core counts doubled at a slower rate
as before after L3 caches emerged.
Why transistor counts rose slower than predicted by Moore’s law?

## Slide 183: 4. Evolution of high-end 2S server processors (15)
With arriving the L3 cache in the 7400 (Dunnington) server processor, the transistor
count rose substantially, from 582 million to 1.9 billion causing much more
dissipation, as shown in the previous Table.
Nevertheless, at the same time the die area was notable enlarged (from
286 mm2 to 503 mm2) providing greatly better cooling conditions.
Subsequently, however next server processor generations were restricted to about
the same silicon area of 500 - to 700 mm2 since technology limitations restrained
a further significant enlarging of the die area as higher error rates would greatly
reduce yields.
Consequently, no notable additional die area was available for better cooling,
so subsequently dissipation became the limiting factor for raising transistor counts
allowing transistor counts and in line with it core counts to double only in about
every four years.
This means that Moore’s law might only be valid as long as dissipation does not
become the limiting factor.
Remark Why the grows rate of transistor counts did not follow Moore’s law after
L3 caches appeared?

## Slide 184: 4. Evolution of high-end 2S server processors (16)
Core count
2006
2008
2010
2012
2014
2016
Year
Nehalem-EX
(45 nm)
Westmere-EX
(32 nm)
Ivy-Bridge-EX
(22 nm)
Broadwell-EP
(14 nm)
*
*
*
*
*
2
4
8
18
28
24
10
6
15
*
*
~2x/4 years
Emergence of
L3 caches in Core 2-based
high-end 2S processor lines
*
Haswell-EP
(22 nm)
12
2018
56
*
Cascade Lake-AP
(Two dies)
(14 nm)
2020
40
*
*
Skylake-SP
Platinum/Gold
(14 nm)
*
Cascade Lake-SP
Platinum/Gold
(14 nm)
Ice Lake-SP
(10 nm)
~2x/2 years
*
5100
(Core 2-based)
(65 nm)
Two-die
implementations
5400
(Penryn b.)
(45 nm)
5300
(Core 2 b.)
(65 nm)
DP 2.8 GHz
(Pentium 4 b.)
(90 nm)
c) Delay in raising core counts due to Intel’s IC fabrication difficulties -1

## Slide 185: 4. Evolution of high-end 2S server processors (17)
c) Delay in raising core counts due to Intel’s IC fabrication difficulties -2
While Intel transitioned to the 10 nm technology, it encountered unexpected difficulties
causing about two years delay to resume the previous rate of doubling core
counts in about four years.

## Slide 186: 4. Evolution of high-end 2S server processors (18)
In contrast: The growth rate of memory speeds in Intel’s HE server processors -1
Transfer rate
(MT/s)
50
100
500
Year
05
2004
06
07
08
1000
3000
200
2000
~ 2*/4 years
09
11
2010
12
13
15
DDR3
1067

14
~ 2*/8 years
x
x
x
x
DDR
400
DDR2
667
DDR3
1600
2S
Emergence of
DDR3 memory
16
17
x
DDR4
2400
DDR4
2933
Emergence of
DDR4 memory
19
18
2020
DDR3
1333
x
x
x
DDR4
2666
DDR4
3200
x

## Slide 187: 4. Evolution of high-end 2S server processors (19)
As the above Figure shows, both memory speeds and core counts has been raised
in two different rates.
In contrast: The growth rate of memory speeds in Intel’s HE server processors -2
Initially, while using DDR and DDR2 memories, memory transfer rates were
doubled roughly in four years.
But after DDR3 memories emerged the growth rate of memory transfer rates
slowed down to doubling rougly every eight years due to the higher complexity
of this technology.
Note that in the considered time interval memory transfer rates have always
been risen approximately at the half rate compared to the growth rate of core
counts.

## Slide 188: 4. Evolution of high-end 2S server processors (20)
What are the implications when memory transfer rates rise slower than
core counts over server generations?
When however memory transfer rates (TM) rise slower than core counts (nC),
the per-core-memory bandwidth (BWM/nC) of a server processor with nM
w-byte wide memory channels
BWM/core = nM ∗ w ∗ TM /nC
obviously decreases since the ratio of TM /nC becomes smaller over time and
thus a memory bandwidth gap would arise.

## Slide 189: 4. Evolution of high-end 2S server processors (21)
The requirement for scaling the memory bandwidth with the core count
As cores operate independently from each other, the per core memory bandwidth
needs to be preserved, i.e. a processor with n-times more cores as a reference
platform requires n-times higher bandwidth as the reference platform, in other words
the memory bandwidth needs to be linearly scaled with the core count.

## Slide 190: 4. Evolution of high-end 2S server processors (22)
How per-core memory bandwidth may be preserved when over generations
memory transfer rates rise slower than core counts?
may be preserved by properly increasing the number of memory channels (nC) such that the expression
nM ∗ TM /nC
remains constant.
BWM/core = nM ∗ w ∗ TM /nC
If however TM /nC decreases
the per core memory bandwidth

## Slide 191: 4. Evolution of high-end 2S server processors (23)
How many memory channels (nM) are needed per socket for preserving
the per core memory bandwidth of an n-core high-end 2S server?
nC | nM
2 | 2.0
4 | 2.8
6 | 3.5
8 | 4.0
10 | 4.5
12 | 4.9
14 | 5.3
16 | 5.6
20 | 6.3
24 | 6.9
32 | 8.0
48 | 9.8
64 | 11.3
Table: The number of memory channels (nM) needed
per socket for preserving the per core memory bandwidth of a high-end server with nC cores
The calculated number of memory channels per socket
(nM) needed are shown in the Table below.
If core counts and memory speeds are assumed to raise at the rate as discussed
before, it can be shown that a high-end server with nC cores needs
approximately nM = √2 ∗ √n memory channels per socket for preserving the
per core memory bandwidth related to a selected reference platform [29].
The calculated number of memory channels per socket
(nM) needed are shown in the Table below.

## Slide 192: 4. Evolution of high-end 2S server processors (24)
What is the key challenge in designing memory systems of server processors? -1
As core counts are continuously raising, more and more memory channels are
needed to compensate for slower rising memory speeds than core counts are
rising.
It is however a quite intricate task to raise the number of memory channels due to
electrical and physical constraints, not discussed in this Chapter, so providing
enough memory channels i.e. memory bandwidth per socket, is one of the key
challenges in designing server processors and platforms.
How far Intel has succeeded in this point is shown in the next Table that states
the number of memory channels and achieved per-core memory bandwidth
(relative to a chosen reference platform) in their high-end 2S server platforms.

## Slide 193: 4. Evolution of high-end 2S server processors (25)
PlatformPer | Core | Techn. | Date of Intro. | High-end multicore 2S server lines | Core count (up to) | Per socket mem. channels (up to) | Per core BW rel. to ref. platform
Reference platform | Pentium 4 Prescott DP | 90 nm | 6/2004 | 90 nm Nocona | 1C | 1x DDR2/400 | 1.0
 | Pentium 4 Presc. | 90 nm | 10/2005 | Xeon DP 2.8 (Paxville DP) | 2x1C | 1x DDR2/400 | 0.5
Bensley | Pentium 4 Presc. | 65 nm | 5/2006 | Xeon 5000 (Dempsey) | 2x1C | 2x DDR2/667 | 1.7
 | Core2 | 65 nm | 6/2006 | Xeon 5100 (Woodcrest) | 2C | 2x DDR2/667 | 1.7
 | Core2 | 65 nm | 11/2006 | Xeon 5300 (Clowertown) | 2x2C | 2x DDR2/667 | 0.8
 | Penryn | 45 nm | 11/2007 | Xeon 5400 (Harpertown) | 2x2C | 2x DDR2/667 | 0.8
Tylersburg | Nehalem | 45 nm | 3/2009 | Xeon 55xx (Gainestown) | 4C | 3x DDR3/1333 | 2.5
Boxboro-EX | Nehalem | 45 nm | 3/2010 | Xeon X6500 Nehalem-EX) | 8C | 8x DDR3/1066 | 2.7
 | Westmere | 32 nm | 4/2011 | Xeon E7-28xx (Westmere-EX) | 10C | 8x DDR3/1333 | 2.7
Brickland | Ivy Bridge | 22 nm | 2/2014 | Xeon E7-28xx v2 (Ivy Bridge-EX) | 15C | 8x DDR3/1600 | 2.1
Grantley | Haswell | 22 nm | 9/2014 | Xeon E5-2600xx v3 (Haswell-EP) | 18C | 4x DDR4/2133 | 1.2
 | Broadwell | 14 nm | 4/2016 | Xeon E5-26xx v4 (Broadwell-EP) | 22C | 4x DDR4/2400 | 1.1
Purley | Skylake | 14 nm | 7/2017 | Xeon Platinum (8176/80 Skylake-SP) | 28C | 6x DDR4/2666 | 1,4
 | Cascade Lake | 14 nm | 4/2019 | Xeon Platinum 8276/80 (Cascade Lake-SP) | 28C | 6x DDR4/2933 | 1.6
Whitney | Sky Lake | 10 nm | 4/2021 | Xeon Platinum 8380 (Ice Lake-SP) | 40C | 8x DDR4-3200 | 1.6
Achieved per core relative bandwidth in Intel’s high end 2S server platforms
1

## Slide 194: 4. Evolution of high-end 2S server processors (26)
As seen, Intel could preserve the per core memory bandwidth, obviously with certain deviations, even increase it in their high-end 2S server processors.
What is the key challenge in designing memory systems of server processors? -2

## Slide 195: 4. Evolution of high-end 2S server processors (27)
Platform | HE multicore 2S server models | Techn. | Date of Intro. | Core count (up to) | PCIe | No./speed of mem. channels per socket (up to) | TDP (up to) W | Socket
Tylersburg | Xeon E55xx (Nehalem –EP) Gainestown) | 45 nm | 3/2009 | 4C | 36x PCIe 2.0 (on MCH) | 3x DDR3-1333 | 95 | LGA 1366
Boxboro-EX | Xeon E65xx Nehalem-EX) (Beckton) | 45 nm | 3/2010 | 8C | 36x PCIe 2.0 (on MCH) | 8x DDR3-1066 | 130 | LGA 1567
 | Xeon E7-28xx (Westmere-EX) | 32 nm | 4/2011 | 10C |  | 8x DDR3-1333 | 130 | 
Brickland | E7-28xx v2 (Ivy Bridge-EX) | 22 nm | 2/2014 | 15C | 32x PCIe 3.0 (on proc.) | 8x DDR3-1600 | 155 | LGA 2011-1
Grantley | E5-26xx v3 (Haswell-EP) | 22 nm | 9/2014 | 18C | 40x PCIe 3.0 (on proc.) | 4x DDR4-2133 | 160 | LGA 2011-3
 | E5-26xx v4 (Broadwell-EP) | 14 nm | 4/2016 | 22C |  | 4x DDR4-2400 | 300 | 
Purley | Xeon Platinum 8176/8180 (Skylake-SP) | 14 nm | 7/2017 | 28C | 48x PCIe 3.0 (on proc.) | 6x DDR4-2400 | 105 | LGA 3647
 | Xeon Platinum 8276/80 (Cascade Lake-SP) | 14 nm | 4/2019 | 28C | 48x PCIe 3.0 (on proc.) | 6x DDR4-2400 | 205 | 
 | Platinum 9282 (Cascade Lake-AP) | 14 nm | 4/2019 | 2x28 | 40x PCIe 3.0 (on proc.) | 12x DDR4-2933 | 400 | BGA 5903
 | Xeon Gold 6238R/58R (Cascade Lake-SP) | 14 nm | 2/2020 | 28C | 48x PCIe 3.0 (on proc.) | 6x DDR4-2933 | 205 | LGA 3647
Whitney | Xeon Platinum 8380 Eis Lake-SP | 10 nm | 4/2021 | 40C | 64xPCIe4.0 (on proc) | 8x DDR4-3200 | n.a. | LGA 4189
TDP values and socketing of Intel’s high-end 2S NUMA server processors -1

## Slide 196: 4. Evolution of high-end 2S server processors (27)
TDP values and socketing of Intel’s high-end 2S NUMA server processors -2
As the previous Table shows, high-end 2S servers have considerable higher TDP
values as typical desktops, ranging typically from 130 W in early server processors
to about 200 W in recent ones.
Note that subsequent server generations implement more and more memory
channels and PCIe lanes, their sockets require more and more pins,
as an example the 10 nm Eis Lake-SP server processor (2021) already has
LGA 4189 sockets.

## Slide 197: 4. Evolution of high-end 2S server processors (28)
Summing up key issues of the evolution of 2S high-end server processors -1
Raising the core count in Intel’s high-end 2S server processors
Doubling core counts in early L3-less high-end Core 2-based 2S server processors about biannually
Introductory remarks
Recently, 2S servers dominate by far the server market (by about 80%).
Contemporary high-end 2S server processors might have a die area of 600-700 mm2
and include much more than 10 billion transistors.
Intel rose the core count in their 2S server processors at two different rates,
as follows:
Doubling core counts in the first phase of the evolution roughly biannually is quite
evident in the light of Moore’s rule, since the evolution of IC technology allowed
doubling transistor counts and consequently core counts as well, roughly every
two years.
This evolution however ended when L3 caches appeared and occupied large parts
of the silicon area.

## Slide 198: 4. Evolution of high-end 2S server processors (29)
b) Slowing down the growth rate of core counts in high-end 2S server processors
after L3 caches emerged
Summing up key issues of the evolution of 2S high-end server processors -2
c) Delay in raising core counts due to Intel’s IC fabrication difficulties
After L3 caches emerged, the evolution of core counts slowed down to a rate of
doubling approximately every four years.
The reason why transistor counts rose slower than predicted by Moore’s law is
the power budget limitation of the die.
At the same time this is also the reason why core counts doubled at a slower rate
as before after L3 caches emerged.
While Intel transitioned to the 10 nm technology, it encountered unexpected difficulties
causing about two years delay to resume the previous rate of doubling core
counts in about four years.

## Slide 199: 4. Evolution of high-end 2S server processors (30)
In contrast: The growth rate of memory speeds in Intel’s HE server processors
What are the implications when memory transfer rates rise slower than
core counts over server generations?
Summing up key issues of the evolution of 2S high-end server processors -3
Initially, while using DDR and DDR2 memories, memory transfer rates were
doubled roughly in four years.
But after DDR3 memories emerged the growth rate of memory transfer rates
slowed down to doubling rougly every eight years due to the higher complexity
of this technology.
Note that in the considered time interval memory transfer rates have always
been risen approximately at the half rate compared to the growth rate of core
counts.
When however, memory transfer rates (TM) rise slower than core counts (nC),
the per-core-memory bandwidth (BWM/nC) of a server processor with nM
w-byte wide memory channels
BWM/core = nM ∗ w ∗ TM /nC
obviously decreases since the ratio of TM /nC becomes smaller over time and
thus a memory bandwidth gap would arise.

## Slide 200: 4. Evolution of high-end 2S server processors (31)
The requirement for scaling the memory bandwidth with the core count
How per-core memory bandwidth may be preserved when over generations
memory transfer rates rise slower than core counts?
Summing up key issues of the evolution of 2S high-end server processors -4
As cores operate independently from each other, the per core memory bandwidth
needs to be preserved, i.e. a processor with n-times more cores as a reference
platform requires n-times higher bandwidth as the reference platform, in other words
the memory bandwidth needs to be linearly scaled with the core count.
BWM/core = nM ∗ w ∗ TM /nC
Decreasing per core memory bandwidths (BWM/nC) however, may be compensated
by properly increasing the number of memory channels (nC) such that the
expression
nM ∗ TM /nC
becomes preserved.
remains constant and thus the per core memory bandwidth

## Slide 201: 4. Evolution of high-end 2S server processors (32)
How many memory channels (nM) are needed per socket for preserving
the per core memory bandwidth of an n-core high-end 2S server?
Summing up key issues of the evolution of 2S high-end server processors -5
If core counts and memory speeds are assumed to raise at the rate as discussed
before, it can be shown that a high-end server with nC cores needs
approximately nM = √2 ∗ √n memory channels per socket for preserving the
per core memory bandwidth related to a selected reference platform [29].
It is however a quite intricate task to raise the number of memory channels due to
electrical and physical constraints, not discussed in this Chapter, so providing
enough memory channels i.e. memory bandwidth per socket, is one of the key
challenges in designing server processors and platforms.
As the evolution of high-end Core 2-based 2S server processors indicates, Intel
could preserve the per core memory bandwidth, obviously with certain deviations,
even increase it in their high-end 2S server processors.

## Slide 202
5. Evolution of tablet and smartpthone processors
Notes: 202

## Slide 203: 5. Evolution of tablet and smartphone processors (1)
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smarphones
Servers
High-End Desktops
Desktops
Laptops
Tablets
Smartphones
Desktops
Smarphones
Servers
Recent major processor categories of Intel
Atom lines
Xeon E7/E5/E3
Platinum/Gold etc.
Desktops/Laptops
(Clients)
Core i9/i7/i5/i3
(Basic architectures)
Atom lines
(+ LP Core models)
HEDTs
(High-End Desktops)
Core i7/i9
(Extreme Edition
or X models)
5. Evolution of tablet and smartphone processors
Mobiles
(Tablets/Smartphones)
Remark
Both Intel and AMD designate laptop processors as mobile processors as well.

## Slide 204: 5. Evolution of tablet and smartphone processors (2)
5. Evolution of tablet and smartphone processors (2)
Design paradigm of mobile processors
As mobile devices require long operating hours, with the advent of mobile devices
(about 2000) a new design paradigm arose that aims at low power consumption,
rather than at highest performance achievable from a given power budget,
as indicated below.
High performance/power
(e.g. GFLOPS/Watt)
Traditional processors
Tablets and smartphones
Low power
(Watt)
(Number of operating hours)

## Slide 205: 5. Evolution of tablet and smartphone processors (3)
Key features of low power microarchitectures at the time of the introduction
of mobiles
Key features of low power microarchitectures at the time of the introduction of mobiles
b) Low clock rates
a) Narrow CPU cores

## Slide 206: 5. Evolution of tablet and smartphone processors (4)
a) Narrow CPU cores in early mobile processors
Early smartphones emerged in the second halve of the 2000’ and were mostly
based on ARM’s 32-bit 2- or 3 wide Cortex processors, as the next Figure
demonstrates.

## Slide 207: 5. Evolution of tablet and smartphone processors (5)
2005
2007
2010
2009
(A9 replacement
for low-end
devices)
32-bit
Width of ARM’s 32-bit CPUs used in most early tablets and smartphones [30]

## Slide 208: 5. Evolution of tablet and smartphone processors (6)
By contrast, width of CPU cores of Intel’s client processors at the time of
the introduction of mobiles
Figure: Width of the cores in Intel’s Core 2 to Haswell processors underlying
servers to laptops [30]
(2006-2013)
At the same time when 32-bit mobile phones and later tablets emerged (≈ 2006-2010)
Intel’s and AMD’s client processors had a word length of 64-bit, were 4 and 3-wide,
respectively, and were designed to achieve high performance/power (in terms of
GFLOPS/Watt), as indicated below.

## Slide 209: 5. Evolution of tablet and smartphone processors (7)
Consequences for Intel and AMD-1
As a consequence, both Intel and AMD were forced to design and introduce new,
narrow (e.g. 2-wide) low-power microarchitectures, as seen in the next two
Figures.
Due to their differing design orientation Intel’s and AMD’s client processors had
much higher power consumption than ARM’s Cortex-processors and were not
suited for mobile devices.

## Slide 210: 5. Evolution of tablet and smartphone processors (8)
Emergence of Intel’s Atom line aiming for tablets and smartphones (Based on [31])
2008
2-wide
in-order
4-wide
out-of-order
2-wide
in order
2-wide
out-of-order
2-wide
in-order
2-wide
out-of-order
2-wide
out-of-order
3-wide
out-of-order
5

## Slide 211: 5. Evolution of tablet and smartphone processors (9)
2014
4/2014
2-wide
out-of-order
2-wide
out-of-order
2-wide
out-of-order
4-wide
out-of-order
Emergence of AMD's Cat line aiming for tablets and smartphones (Based on [31])

## Slide 212
5. Evolution of tablet and smartphone processors (10)
b) Low clock rates in early mobile processors
Power consumption = Active power Dd = Cdyn∗VCC2 ∗ fc + Leakage power Ds = VCC ∗ Ileak
Let’s consider the basics of power consumption of CPUs.
Figure: Example: Core voltage (VCC) vs. clock frequency (fC) for Intel’s
Westmere processors [32]
In addition: higher fc requires higher VCC (VCC ≈ const x fC), as indicated below.

## Slide 213: 5. Evolution of tablet and smartphone processors (11)
Relative high base frequency
(typically 2-4 GHz)
Client CPUs
Mobile CPUs
Relative low base frequency
(typically 1.5 -2.5 GHz)
Allow lower power budget
Allow higher power budget
The relation of clock frequency (fc) and dynamic dissipation Dd
As Dd = const x Vcc2 ∗ fc and Vcc = const ∗ fc, it follows that
Dd = const ∗ fc3
This means that the dynamic dissipation rises very vital with the clock frequency,
in fact it rises proportional to the third power of fc.
As a consequence the available power budget of the processors (usually given
in form of their TDP), limits their base frequency, as indicated below.

## Slide 214
TDP (W) | No. of cores | Graphics | No. of graphics EUs | eDRAM | Base frequency (GHz)
4.5 | 2 | HD 515 | 18 | -- | 1.2
15 | 2 | HD 540 | 48 | 64 MB | 2.2
15 | 2 | HD 520 | 24 | -- | 2.6
28 | 2 | HD 550 | 48 | 64 MB | 3.3
35 | 4 | HD 530 | 24 | -- | 2.8
45 | 4 | HD 530 | 24 | -- | 2.9
65 | 4 | HD 530 | 24 | -- | 3.4
91 | 4 | -- | -- | -- | 4.2
Example for restricting the max. clock frequency by the TDP value in
Skylake desktop models of the Core 2 family (Based on data from [33])
5. Evolution of tablet and smartphone processors (12)

## Slide 215: 5. Evolution of tablet and smartphone processors (13)
Clock rates of early mobile processors
The low power budget of early mobile processors limited their base frequency
to about 1.0 to 2.0 GHz.

## Slide 216: 5. Evolution of tablet and smartphone processors (14)
The tale of Intel’s Atom line
As an example, the next Figure shows Intel’s smartphone platforms developed and
marketed.
Note that these platforms (except the latest implementations) used extra discrete
(XMM) modems), whereas most competing platforms (except Apple’s devices)
included already integrated modems.
Based on their Atom line Intel developed a large number of smartphone and
tablet platforms to gain a respectable market share in the mobile space.

## Slide 217: 5. Evolution of tablet and smartphone processors (15)
Intel’s Atom-based smartphone platforms (based on [34])
Eul H., & Bell M., Mobile at Intel, Investor Meeting 2012, Intel,
http://www.cnx-software.com/pdf/Intel_2012/2012_Intel_Investor_Meeting_Eul_Bell.pdf
Clover Trail+
(2013)
Medfield
(2012)
Merrifield
(2014)
Moorefield
(2014)
Lexington
(2013)
Slayton
(2014)
Z2520-2580
2x Saltwell
32 nm
+XMM 6268/6360/7160
Z2420
1x Saltwell
32 nm
+XMM 6265
Z2460/2480
1x Saltwell
32 nm
+XMM 6260
Z34x0
2x Silvermont
22 nm
+XMM 7160/7260
Z3xxx
2x Silvermont
22 nm
+A-GOLD 620
Z35xx
4x Silvermont
22 nm
+XMM 7260/2/35
Performance (not to scale)
Morestown
(2010)
Z6xx
1x Bonnell
45 nm
+Wireless
module
Riverton
(2015)
SoFIA
(x3 3G/LTE)
(2015)
Z3xxx
2x Airmont
14 nm
Integrated
LTE modem
C31xx/32xx/34xx
2x/4x Silvermont
28 nm
Integrated LTE
3G/4G modem
Planned, not mplemented
Cancelled
in 04/2016
Planned, not implemented
Morganfield
(2016)
Z5xxx
4x Goldmont
14 nm
+XMM 7360
Cancelled
in 04/2016

## Slide 218: 5. Evolution of tablet and smartphone processors (16)
Intel’s effort to optimize their platforms from the software point of view
In their 2012 Investor meeting (5/2012) Intel revealed that more than 3000
engineers are working on OS support, among them about 1200 engineers
are dedicated alone to Android, as indicated below [35].

## Slide 219: 5. Evolution of tablet and smartphone processors (17)
Intel’s worldwide market share of smartphone and tablet application processors
in 2015, (based on revenue) [36]
Smartphone application processors worldwide market share 2015 (revenue) | 
Qualcomm (USA) | 42 %
Apple (USA) | 21 %
MediaTek (Taiwan) | 19 %
Samsung (S. Korea) | 
Spreadtrum (China) | 
Tablet application processors worldwide market share 2015 (revenue) | 
Apple (USA) | 31 %
Qualcomm (USA) | 16 %
Intel (USA) | 14 %
MediaTek (Taiwan) | 
Samsung (S. Korea) | 
[Source: Related press releases of Strategy Analytics]
As the Table on the left side indicates, Intel did not achieve a notable smartphone
market share.
Nevertheless, Intel reached a 14 % market share for tablet processors, but this
has been achieved by paying subsidies for OEMs (~ 50 $ /processor) to spurn
a transition from ARM to Atom processors.

## Slide 220: 5. Evolution of tablet and smartphone processors (18)
Intel's losses on mobile devices in 2013 - 2014 [37]
Owing to paying subsidies to OEMs, Intel's mobile and communication division lost
7 billion $ in the years 2013-2014 , as indicated in the next Figure [38].
Figure: Revenues/operating income of Intel's Mobile and Communications segment
2013-2014 [38]

## Slide 221: 5. Evolution of tablet and smartphone processors (19)
Intel's withdrawal from the smartphone and mobil market [39] -1
"I can confirm that the changes included canceling the Broxton platform as well as
SoFIA 3GX, SoFIA LTE and SoFIA LTE2 commercial platforms to enable us to move resources to products that deliver higher returns and advance our strategy.
These changes are effective immediately.“ (See next Figure).
Intel's statement says:
Due to their high losses Intel first stopped paying subsidies and then in 4/2016 announced their withdrawal from the mobile market.

## Slide 222: 5. Evolution of tablet and smartphone processors (20)
Cancellation of Intel’s Atom-based smartphone platforms (based on [40])
Eul H., & Bell M., Mobile at Intel, Investor Meeting 2012, Intel,
http://www.cnx-software.com/pdf/Intel_2012/2012_Intel_Investor_Meeting_Eul_Bell.pdf
Clover Trail+
(2013)
Medfield
(2012)
Merrifield
(2014)
Moorefield
(2014)
Lexington
(2013)
Slayton
(2014)
Z2520-2580
2x Saltwell
32 nm
+XMM 6268/6360/7160
Z2420
1x Saltwell
32 nm
+XMM 6265
Z2460/2480
1x Saltwell
32 nm
+XMM 6260
Z34x0
2x Silvermont
22 nm
+XMM 7160/7260
Z3xxx
2x Silvermont
22 nm
+A-GOLD 620
Z35xx
4x Silvermont
22 nm
+XMM 7260/2/35
Performance (not to scale)
Morestown
(2010)
Z6xx
1x Bonnell
45 nm
+Wireless
module
Riverton
(2015)
SoFIA
(x3 3G/LTE)
(2015)
Z3xxx
2x Airmont
14 nm
Integrated
LTE modem
C31xx/32xx/34xx
2x/4x Silvermont
28 nm
Integrated LTE
3G/4G modem
Planned, not mplemented
Cancelled
in 04/2016
Planned, not implemented
Morganfield
(2016)
Z5xxx
4x Goldmont
14 nm
+XMM 7360
Cancelled
in 04/2016

## Slide 223: 5. Evolution of tablet and smartphone processors (21)
Intel's withdrawal from the smartphone and mobil market [39] -2
At the same time Intel laid off about 12000 employees (~ 11 % of their workforce).

## Slide 224: 5. Evolution of tablet and smartphone processors (22)
AMD’s cancellation of their Cat line in 2015
The last core of AMD's Cat line was the Puma+ core (launched in 6/2015 in the
Carrizo-L APU).
Subsequently, there was no sign for continuing the Cat line.
Instead AMD placed emphasis on the Zen architecture that has been launched
in 2017.

## Slide 225: 5. Evolution of tablet and smartphone processors (23)
Nvidia’s leaving the smartphone and tablet market in June 2016 [41]
Instead NVIDIA became interested in designing in-car computers and car
infotainment systems beyond their traditional field of discrete GPU cards (dGPUs).
“We are no longer interested in that market”. He adds, “Anybody can build smartphones, and we’re happy to enjoy these devices, but we’ll let someone else build them”.
In 6/2016 (at Computex) NVIDIA's CEO J. Huang declared the firm's leaving the
smartphone and tablet market by saying:

## Slide 226: 5. Evolution of tablet and smartphone processors (24)
Remark to the evolution of the width of mobile CPU cores -1
ARM’s early mobile processors were 32-bit designs and usually 2- or 3-wide,
subsequent mobile processors first became 64-bit designs (since about 2012)
followed by an impressive widening of their microarchitecture, as indicated in the
next Figures.
Here we note that certain early mobile processors were only 1-wide, like
ARM’s 1176 used in Apple’s iPhone (2007) or
ARM’s Cortex-A5 (2009)
nevertheless, for better clarity these processors are not indicated in the next
Figure.

## Slide 227: 5. Evolution of tablet and smartphone processors (25)
Remark to the evolution of the width of mobile CPU cores -2
3-wide
2-wide
4-wide
Width of mobile cores
(or of big cores of big.LITTLE or dynamIQ core clusters)
5-wide
ARM
v7 Cortex-A (2005-09)
(except 1-wide LP A5 (2009)
and 3-wide HP A15))
v7 HP Cortex-A15
(2010)
Intel
Atom family (2008-15)
AMD
Cat family (2011-2015)
Apple
v7 Cortex-A8 (2009)
v7 Swift (A6) (2012)
Qualcomm
v7 Scorpion
(S1-S3) (2007-10)
v7 Krait
(S4/S400/S60x/S80x)
(2012-14)
v8 Kryo/Kryo 280
(S820/821/835) (2015/2016/2017)
v8.2 Kryo 385
(S845) (2018)
Samsung
v8.0 M1 (2016)
(Exynos 8 Octa)
v8 M2 (2017)
(Exynos 9 Octa)
v8.0 HP Cortex-A (2013-15) (except 2-wide HP Cortex-A73)
v7 Exynos 5
(2013-14)
v8 Exynos 7
(2016)
v8.2 HP Cortex-A76
(2018) to
HP Cortex-A78
(2020)
HP: High-Performance/big core
LP: Low-Power
v8.0 HP Cortex-A73
(2016)
Airmont-based Atom core (2016)
v8.0/8.2 LP Cortex-A
(2013/2017)
v8.2 HP Cortex-A75
(2017)
v8.2 HP Cortex-X1
(2020))

## Slide 228: 5. Evolution of tablet and smartphone processors (26)
Remark to the evolution of the width of mobile CPU cores -3
6-wide
7-wide
Width of mobile cores
(or of big cores of big.LITTLE or dynamIQ core clusters)
8-wide
ARM
Intel
AMD
Apple
Qualcomm
Samsung
HP: High-Performance/big core
LP: Low-Power
v8.0 HP A7-A10X
(2013-2017)
v8.2 HP A11 (2017)
v8.3 HP A12/A12X
(2018)
v8.4 HP A13 (2019)
v8.6 HP A14/M1
(2020)
v8.2 M6
(2020)/cancelled
v8.2 M3 (2018) Exynos 9810)
v8.2 M4 (2019) Exynos 9820)
v8.2 M5 (2019) Exynos 990)

## Slide 229: 5. Evolution of tablet and smartphone processors (27)
Changing the design paradigm of mobile processors
As mobile devices require long operating hours, with the advent of mobile devices
(about 2006) a new design paradigm arose that aims at low power consumption,
rather than at highest performance achievable from a given power budget,
as indicated below.
High performance/power
(e.g. GFLOPS/Watt)
Traditional processors
Tablets and smartphones
Low power
(Watt)
(Number of operating hours)
Summing up key issues of the evolution of tablet and smartphone processors -1
Key features of low power microarchitectures at the time of the introduction
of mobiles
Key features of low power microarchitectures at the time of the introduction of mobiles
b) Low clock rates
a) Narrow CPU cores

## Slide 230: 5. Evolution of tablet and smartphone processors (28)
a) Narrow CPU cores in early mobile processors
Early smartphones emerged in the second halve of the 2000’ and were mostly
based on ARM’s 32-bit 2- or 3 wide Cortex processors.
By contrast, the width of CPU cores of Intel’s client processors at the time
of the introduction of mobiles
At the same time when 32-bit mobile phones and later tablets emerged (≈ 2006-2010)
Intel’s and AMD’s client processors had a word length of 64-bit, were 4 and 3-wide,
respectively, and were designed to achieve high performance/power (in terms of
GFLOPS/Watt).
Consequences for Intel and AMD
As a consequence, both Intel and AMD were forced to design and introduce new,
narrow (e.g. 2-wide) low-power microarchitectures,.
Due to their differing design orientation Intel’s and AMD’s client processors had
much higher power consumption than ARM’s Cortex-processors and were not
suited for mobile devices.
Summing up key issues of the evolution of tablet and smartphone processors -2

## Slide 231: 5. Evolution of tablet and smartphone processors (29)
b) Low clock rates in early mobile processors
Power consumption = Active power Dd = Cdyn∗VCC2 ∗ fc + Leakage power Ds = VCC ∗ Ileak
In addition: higher fc requires higher VCC (VCC ≈ const x fC), as indicated below.
The relation of clock frequency (fc) and dynamic dissipation Dd
As Dd = const x Vcc2 ∗ fc and Vcc = const ∗ fc, it follows that
Dd = const ∗ fc3
This means that the dynamic dissipation rises very vital with the clock frequency,
in fact it rises proportional to the third power of fc.
As a consequence the available power budget of the processors (usually given
in form of their TDP), limits their base frequency.
Clock rates of early mobile processors
The low power budget of early mobile processors limited their base frequency
to about 1.0 to 2.0 GHz.
Summing up key issues of the evolution of tablet and smartphone processors -3

## Slide 232: 5. Evolution of tablet and smartphone processors (30)
The tale of Intel’s Atom line
Based on their Atom line Intel developed a large number of smartphone and
tablet platforms to gain a respectable market share in the mobile space.
Intel did not achieve a notable smartphone market share.
Nevertheless, Intel reached a 14 % market share for tablet processors, but this
has been achieved by paying subsidies for OEMs (~ 50 $ /processor) to spurn
a transition from ARM to Atom processors.
Due to their high losses Intel first stopped paying subsidies and then in 4/2016
announced their withdrawal from the mobile market.
Summing up key issues of the evolution of tablet and smartphone processors -4
Intel’s worldwide market share of smartphone and tablet application processors
in 2015
Intel's withdrawal from the smartphone and mobil market [39] -1

## Slide 233: 5. Evolution of tablet and smartphone processors (31)
AMD’s cancellation of their Cat line in 2015
The last core of AMD's Cat line was the Puma+ core (launched in 6/2015 in the
Carrizo-L APU).
Subsequently, there was no sign for continuing the Cat line.
Instead AMD placed emphasis on the Zen architecture that has been launched
in 2017.
Nvidia’s leaving the smartphone and tablet market in June 2016 [41]
In 6/2016 (at Computex) NVIDIA's CEO J. Huang declared the firm's leaving the
smartphone and tablet market.
Summing up key issues of the evolution of tablet and smartphone processors -5

## Slide 234
6. References
Notes: 234

## Slide 235: 6. References (1)
[5]: Fisher S., “Technical Overview of the 45 nm Next Generation Intel Core Microarchitecture
(Penryn),” IDF 2007, ITPS001, http://isdlibrary.intel-dispatch.com/isd/89/45nm.pdf
[6]: Server duel: Xeon Woodcrest vs. Opteron Socket F, Tweakers, Sept. 7 2006,
https://tweakers.net/reviews/646/2/server-duel-xeon-woodcrest-vs-opteron-socket-f-
post-mortem-netburst.html
[7]: Razin A., Core, Nehalem, Gesher. Intel: New Architecture Every Two Years,
Xbit Laboratories, April 28 2006,
http://www.xbitlabs.com/news/cpu/display/20060428162855.html
[1]: Exynos 8 Octa (8890), Samsung, 2016,
http://www.samsung.com/semiconductor/minisite/Exynos/w/solution/mod_ap/8890
[2]: Shilow A., Intel’s Path to 10nm: Past, Present, and Future, EET Asia, June 17, 2020,
https://www.eetasia.com/intels-path-to-10nm-past-present-and-future
[3]: 10_nm lithography process,
https://en.wikichip.org/wiki/10_nm_lithography_process
[4]: Intel eases up in race to 10GHz, The Register, Sept. 25 2002,
https://www.theregister.co.uk/2002/09/25/intel_eases_up_in_race/
[8]: Intel's (INTC) CEO Brian Krzanich on Q2 2015 Results - Earnings Call Transcript, Seeking
Alpha, July 15 2015, http://seekingalpha.com/article/3329035-intels-intc-ceo-brian-
krzanich-on-q2-2015-results-earnings-call-transcript?page=2
[9]: ARS STAFF; Intel retires “tick-tock” development model, extending the life of each process; https://arstechnica.com/; 03.23.2016; https://arstechnica.com/information-technology/2016/03/intel-retires-tick-tock-development-model-extending-the-life-of-each-process/

## Slide 236: 6. References (2)
[10]: Cutres I.; Intel’s 10nm Cannon Lake and Core i3-8121U Deep Dive Review; anandtech.com; 25. January 2019.; https://www.anandtech.com/show/13405/intel-10nm-cannon-lake-and-core-i3-8121u-deep-dive-review
[11]: Passingham M., Intel 8th-gen CPUs Revealed: Double the cores, but where’s Coffee Lake?,
Trusted Reviews, Aug. 23 2017, http://www.trustedreviews.com/news/intel-8th-gen-
core-specs-technology-explained-2952599
[12]: Cutress I., Intel’s Manufacturing Roadmap from 2019 to 2029: Back Porting, 7nm, 5nm,
3nm, 2nm, and 1.4 nm, AnandTech, Dec. 11, 2019,
https://www.anandtech.com/show/15217/intels-manufacturing-roadmap-from-2019-to-2029
[13]: Papermaster M., Back in High Performance...To Stay, AMD 2017 Financial Analyst Day,
May 16 2017, http://ir.amd.com/phoenix.zhtml?c=74093&p=irol-analystday
[14]: Vireko K., A Simple Guide To Intel CPU/Processor Naming Scheme (Explained), Tech Consumer Guide, Mai 16, 2019, https://www.techconsumerguide.com/guide-to-intel-cpu-naming
[15]: New Xeon Processor Numbering, More Than Just a Number, Intel.com, April 5 2011,
https://communities.intel.com/community/itpeernetwork/datastack/blog/2011/04/05/
new-xeon-processor-numbering-more-than-just-a-number
[16]: Intel Core 2 Duo Processor E8000 and E7000 Series Datasheet, Intel, Jan. 2009
[17]: Morgan t. P. Deep dive into Intel’s “Ice Lake” Xeon SP architecture, The next platform, April 19, 2021,https://www.nextplatform.com/2021/04/19/deep-dive-into-intels-ice-lake-xeon-sp-architecture/
[18]: Bohr M., Leading at the edge, Technology and manufacturing Day, Intel, 28/03/2017,
https://newsroom.intel.com/newsroom/wp-content/uploads/sites/11/2017/03/
Mark-Bohr-2017-Moores-Law.pdf

## Slide 237: 6. References (3)
[19]: Intel 5th Generation Broadwell Processors Arrive, Cherry Trail Shipping; CdrInfo.com; 5. January 2015.; https://www.cdrinfo.com/sections/news/Print.aspx?NewsId=42515
[20]: Wikipedia, Intel HD and Iris Graphics,
https://en.wikipedia.org/wiki/Intel_HD_and_Iris_Graphics
[21]: oneAPI GPU Optimization Guide; Developer Guide; Intel.com; 11. April 2021.; https://www.intel.com/content/www/us/en/develop/documentation/oneapi-gpu-optimization-guide/top/gen-arch.html
[22]: Cutress I., Hot Chips 2020 Live Blog: Intel's Xe GPU Architecture (5:30pm PT), AnandTech,
Aug. 17 2020, https://www.anandtech.com/show/15993/hot-chips-2020-live-blog-intels-
xe-gpu-architecture-530pm-pt
[23]: Simth R.; The Intel XE-LP GPU Architecture Deep Dive; anadtech.com; 13. August 2020.; https://www.anandtech.com/show/15973/the-intel-xelp-gpu-architecture-deep-dive-building-up-from-the-bottom
[24]: Blythe D., Technology Insight: Next Generation Intel Processor Graphics Architecture
Code Name Skylake, SPCS003, IDF15, San Francisco, Aug. 2015
[25]: X299 XPOWER GAMING AC, MSI,
https://www.msi.com/Motherboard/X299-XPOWER-GAMING-AC.html#productSpecification
-section
[26]: Ung G. M., Intel Broadwell-E Core i7-6950X Review: The first 10-core enthusiast CPU is a
beast, PC World, May 30 2016, http://www.pcworld.com/article/3075433/computers/
intel-broadwell-e-core-i7-6950x-review-the-first-10-core-enthusiast-cpu-is-a-monster.html
[27]: A New Day for the Datacenter, Presentation at AMD Financial Analyst Day, May 16 2017,
http://ir.amd.com/phoenix.zhtml?c=74093&p=irol-analystday

## Slide 238: 6. References (4)
[28]: Coffee Lake - Microarchitectures – Intel, WikiChip (visited on 27 Aug., 2019),
https://en.wikichip.org/wiki/intel/microarchitectures/coffee_lake
[29]: Scansen D., Intel Launches Next Generation of Microprocessors, Engineering, June 10 2013,
http://www.engineering.com/ElectronicsDesign/ElectronicsDesignArticles/ArticleID/
5838/Intel-Launches-Next-Generation-of-Microprocessors.aspx
[30]: Wechsler O., “Inside Intel Core Microarchitecture,” White Paper, Intel, 2006
[31]: Bryant D., “Intel Hitting on All Cylinders,” UBS Conf., Nov. 2007,
http://files.shareholder.com/downloads/INTC/0x0x191011/e2b3bcc5-0a37-4d06-
aa5a-0c46e8a1a76d/UBSConfNov2007Bryant.pdf
[32]: Fisher S., “Technical Overview of the 45nm Next Generation Intel Core Microarchitecture
(Penryn),” IPTS001, Fall IDF 2007, http://isdlibrary.intel-dispatch.com/isd/89/45nm.pdf
[33]: Cutress I., The Intel Skylake Mobile and Desktop Launch, with Architecture Analysis,
AnandTech, Sept. 1 2015, http://www.anandtech.com/show/9582/intel-skylake-mobile-
desktop-launch-architecture-analysis
[34]: Eul H., Bell M., Mobile at Intel, Investor Meeting 2012,
http://www.cnx-software.com/pdf/Intel_2012/2012_Intel_Investor_Meeting_Eul_Bell.pdf
[35]: Lee V., “Inside the Intel Core Microarchitecture,” IDF, May 2006, Shenzhen,
http://www.prcidf.com.cn/sz/systems_conf/track_sz/SMC/Intel%20Core%20uArch.pdf
[36]: Qualcomm dominates smartphone chip and baseband, tablet processor markets, Mobile
Europe, February 17 2014
http://www.mobileeurope.co.uk/Press-Wire/qualcomm-dominates-smartphone-chip-and
-baseband-tablet-processor-markets

## Slide 239: 6. References (5)
[37]: Völkel F., “Duel of the Titans: Opteron vs. Xeon : Hammer Time: AMD On The Attack,”
Tom’s Hardware, Apr. 22 2003,
http://www.tomshardware.com/reviews/duel-titans,620.html
[38]: George V., Piazza T., Jiang H.: Technology Insight: Intel Next Generation Microarchitecture
Codename Ivy Bridge, IDF 2011
[39]: Smith R., Intel's Changing Future: Smartphone SoCs Broxton & SoFIA Officially Cancelled,
AnandTech, April 29, 2016,
http://www.anandtech.com/show/10288/intel-broxton-sofia-smartphone-socs-cancelled
[40]: Intel Timna Microprocessor Family, CPU World, http://www.cpu-world.com/CPUs/Timna/
[41]: Olivera, A régóta várt Intel Ivy Bridge tesztje, Prohardware, April 13 2012,
http://prohardver.hu/teszt/intel_ivy_bridge_teszt/az_ivy_bridge.html
[42]: Shimpi a. L. & Smith R., The Intel Ivy Bridge (Core i7 3770K) Review, AnandTech, April 23, 2012,
https://www.anandtech.com/show/5771/the-intel-ivy-bridge-core-i7-3770k-review/4
[43]: Wright A., Intel 12th Gen Alder Lake vs. AMD Ryzen 5000: Which Should You Get?, MUO,
17. Jan., 2021,
https://www.makeuseof.com/intel-12th-gen-vs-amd-ryzen-5000/
[44]: Crider M., Intel 12th-gen ‘Alder Lake’ vs. Ryzen 5000: 5 key things to know, PCWorld, 04. Nov. 2021,
https://www.pcworld.com/article/549847/intel-alder-lake-vs-ryzen-5000-5-things-to-know.html
[45]: Smith R., AMD Details Ryzen 7000 Launch: Ryzen 7950X and More, Coming sept. 27th,
https://www.anandtech.com/show/17552/amd-details-ryzen-7000-launch-up-ryzen-7950x-
coming-sept-27

## Slide 240: 6. References (5)
[46]: Cutress I., AMD Ryzen 5000 and Zen 3 on Nov 5th: +19% IPC, Claims Best Gaming CPU,
AnandTech, Oct. 8, 2020,
https://www.anandtech.com/print/16148/amd-ryzen-5000-and-zen-3-on-nov-5th-19-
ipc-claims-best-gaming-CPU
[47]: Hwang c., TSMC dossier (4): Technology contention among world-class leaders, Digitimes,
17. July, 2021, https://www.digitimes.com/news/a20210713VL201.html
[48]: Cutress I., The Snapdragon 8 Gen 1 Performance Preview: Sizing Up Cortex-X2, AnandTech, Dec. 14, 2021, https://www.anandtech.com/show/17102/snapdragon-8-gen-1-performance-preview-sizing-up-cortex-x2/2
[49]: Frumusanu A., Arm Announces Neoverse V1, N2 Platforms & CPUs, CMN-700 Mesh: More
Performance, More Cores, More Flexibility, anandTech, April 27, 2021,
https://www.anandtech.com/print/16640/arm-announces-neoverse-v1-n2-platforms-
cpus-cmn700-mesh