## Slide 1
Dezső Sima
© Dezső Sima 2024
(v10.1)
The ARM ISA and ARM CPU cores
Lecture
November 2024

## Slide 2: Forword (1)
Preliminary remarks
ARM designs functional units for processors, such as CPU cores, GPUs, NPUs
(Neural Processing Units), MCs (Memory Controllers), on-die interconnects, and more.
ARM plays a pivotal role in the industry by licensing the ARM ISA and IP
(Intellectual Property) of these complex functional unit designs to other companies,
thereby influencing the landscape of processor development.
In contrast, companies, like Intel, AMD, Apple, Samsung, Qualcomm, etc.,
design complete processors based on either the x86- or Arm ISA.
Companies that design ARM ISA-based processors pay for the ARM ISA license and
either create their custom designs or license ARM’s configurable functional unit
designs and build their processors processors using these configurable components.
Additionally, there is also a difference in whether the companies own IC foundries
and manufacture their processor dies in-house (like Intel and Samsung), or
let their processor dies produced by external foundries (such as TSMC).
It is essential to clarify a few basic designations before discussing ARM's designs,
such as illustrated in the following Figure.
IP: Intellectual Property (szellemi termék) On-die interconnect: lapkán megvalósított kapcsolóhálózat

## Slide 3: Forword (2)
GIC: General
Interrupt Controller
Illustration of the terminology used
Figure: An example big.LITTLE processor [2]
Processor
CPU
CPU core
Core cluster
CPU cores are the basic components of processors, such as ARM’s Cortex-A cores.
Multiple CPU cores, along with a shared cache, can be organized into core clusters.
One or multiple core clusters make up a CPU and
a CPU, augmented by additional functional units, like GPUs, NPUs, a Cache Coherent
Interconnect form a processor, as shown in the Figure above.

## Slide 4
Forword (3)
Remark to the terminology
In their presentations and documentation, ARM often refers to CPU cores as CPUs,
which is misleading in multicore designs.
This Chapter specifically discusses CPU cores based on the Armvx-A ISA.
The “A” tag refers to application-oriented CPUs, used in mobile devices, as will be
discussed later.
However, both ARM and our Lecture Notes are inconsequent in using the term
“A tag” as it is not always specified.
But regardless of whether the “A tag” is specified or not, our Chapter consistently
refers to CPUs based on the Armvx-A ISA.
One more point: This Chapter discusses ARM’s CPU core designs, which we often
refer to simply as CPU cores for brevity.

## Slide 5
ARM’s CPU cores
1. Introduction to ARM
2. How has the Arm ISA evolved?
4. References
3. How have ARM’s CPU core designs evolved?
Annex 1: Cache-coherent interconnects
Notes: 5

## Slide 6
1. Introduction to ARM

## Slide 7: 1. Introduction to ARM (1)
1. Introduction to ARM
Intellectual Property: szellemi tulajdon
NPU: Neural Processing Unit
ARM is a British semiconductor design company based in Cambridge.
It was founded in 1990 as Advanced RISC Machines Ltd, which was a joint
venture between Acorn Computers, Apple Computer (now Apple Inc.), and
VLSI Technology (now NXP Semiconductors N.V).
ARM was later acquired by Softbank (Japan) in 2016.
The company specializes in designing low-power processor components for various
markets, including embedded systems, mobile devices, and, since about 2014 the
server market as well.
Their product offerings include Cortex CPUs, Mali GPUs, Ethos NPUs, Memory Controllers (DMC), on-chip interconnects, etc.
Additionally, ARM develops related software tools, such as development studios.
ARM licenses their IP (Intellectual Property), including the Arm ISA, but
does not manufacture semiconductors.
Here, we note that ARM also announced a new CPU family branding called Neoverse
in 2018 for processors and platforms, targeting information infrastructures
such as data centers, routers, switches etc.
This topic is not discussed in this Lecture.

## Slide 8: 1. Introduction to ARM (2)
Graphic IP | Other IP | Tools
ARM Mali™-G71 Mali-DP550 (Display processor) Mali-V550 (Video Processor) | ARM CoreLink™ CCI-550 (Cache Coherent Interconnect) CoreLink GIC-500 (Interrupt Controller) CoreLink MMU-500 (System Memory Management Unit) CoreLink TZC-400 (ARM TrustZone® Controller) CoreLink DMC-500/DMC-520 (Dynamic Memory Controller) ARM CoreSight™ SoC-400 (Debug and Trace) ARM POP™ (Physical IP) | ARM DS-5 Development Studio Fixed Virtual Platforms ARM Versatile™ Express ARM Compiler 6 ARM Fast Models
Example 1: ARM's IP offer related to the Cortex-A73 CPU [3]

## Slide 9: 1. Introduction to ARM (3)
ADB: AMBA Domain Bridge
(to implement DVFS)
Example 2: An Armv8.0-based SoC design that includes Cortex-A57/A53 CPUs
along with the CCI-400 interconnect, developed in 2012 [4] An
Published by ARM and used in LG's Odin/Nuclun SoC.

## Slide 10: 1. Introduction to ARM (4)
Example 3: Armv8.2-based SoC design with Cortex-A75/A55 CPUs and
CCI-550 interconnect (2017) [5]
CCI-550: Cache Coherent interconnect CoreSight: for debug and trace
MMU-500: Memory Management Unit (responsible for virtualization and caching)
NIC-450: Network Interconnect (interface converter)
GIC-600: General Interrupt Controller
SCP: System Control Processor

## Slide 11: 1. Introduction to ARM (5)
ARM's business model [6]
ARM owns and licenses the Arm ISA, designs functional units, and licenses those designs
to semiconductor companies.
ARM receives an initial license fee and, later, collcts a royalty for every chip containing its
technology.
Semiconductor partners manufacture and sell chips to OEMs (Original Equipment
Manufacturers), while OEMs provide feedback to ARM for new design requirements.

## Slide 12: 1. Introduction to ARM (6)
Configurability of ARM’s designs
The Figure below illustrates an example of how a Cortex-A35 may be configured
for a wide range of applications, from mobile to deeply embedded use.
ARM's designs are customizable, allowing, e.g., for selecting L1/L2/L3
cache sizes or core counts.
Figure: Configuration options of a Cortex-A35 CPU [7]
NEON: SIMD unit

## Slide 13: 1. Introduction to ARM (7)
Semi custom design
Full synthesizable design
Approaches to circuit design
Full custom design
Hand layout of the
entire circuit
Automated layout of the
entire circuit
Simple scaling, e.g.
from 28 nm to 16 nm
The design will be subdivided into
functional units and further on into blocks
and the appropriate implementation technique
(hand layout, structured layout or automated layout)
is chosen for each.
Power/performance
optimized
Implementation time
optimized
Evolution of the approaches used for circuit design -1 [8]
Trend

## Slide 14: 1. Introduction to ARM (8)
Over time, more and more advanced standard cell libraries have been developed
with a wide variety of design options, such as cell types or transistor sizes,
reducing or eliminating the need for custom designs.
Before designing the Cortex A9 processor, ARM designs were partly hand layouts
and partly automated layouts.
ARM’s first fully synthesizable design was the Cortex-A9 processor (announced in 2007).
Evolution of the approaches used to circuit design -2 [8]
Nowadays, automated design tools are commonly used for designing processors.
Standard cells are pre-designed building blocks for XOR, AND, OR, or flip-flops
that may be used in designing integrated circuits.

## Slide 15: 1. Introduction to ARM (9)
ARM’s licensing policy [9] -1
ARM provides either a Cortex licence or an Architecture licence.
A Cortex license grants the licensee complete access to a standard microarchitecture
design (IP).
The design is configurable; for instance, the sizes of the L1 or L2 caches are
selectable.
The Architecture license only allows the use of the ARM ISA.
The licensee has to design their custom microarchitecture, which results in a
proprietary CPU.
For example, Apple or Samsung bought Architecture licenses, designed their
CPUs, and named them as they liked.

## Slide 16: 1. Introduction to ARM (10)
ARM’s advanced “Built on ARM Cortex Technology” licensing model [9]
In 02/2016, a new license agreement was introduced exclusively for lead partners.
This agreement allows licensees to request microarchitecture changes
and utilize the customized design in their products.
Additionally, ARM offers engineering and design services for implementing the
requested modifications for additional costs.
Under the license’s terms, ARM still owns the IP; however, the modified
microarchitecture is not shared or made available to other licensees.
Licensees have branding freedom.
An example is Qualcomm’s Kryo 280 CPU, which is based on ARM’s Cortex-A73,
whereas earlier Qualcomm CPUs were custom-designed based on an
Architecture license.

## Slide 17: 1. Introduction to ARM (11)
Evolution of ARM’s products and the total number of ARM based chips shipped [10]
Keil: Software development tool for embedded processors Cortex R: Real-time M: Embedded
Linaro: Nonprofit company established by ARM, Freescale, IBM, Samsung, ST-Ericsson and TI
to support open-source software developers using Linux on SoCs.
SBSA: Server Base System Architecture, a standardized server platform for 64-bit ARM processors.
(FP/FP SIMD)
64-bit)
(Application)
(GPU)

## Slide 18: 1. Introduction to ARM (12)
Number of ARM chips sold annually over time in billions [88]
As shown in the Figure above, approximately 30 billion Arm ISA-based chips are
currently sold annually.

## Slide 19: 1. Introduction to ARM (13)
Total number of ARM-based chips shipped until 10/2021
ARM reported that as of 10/2021, more than 200 billion chips had been shipped
with their ISA [12].

## Slide 20: 1. Introduction to ARM (14)
Why have ARM designs became dominant in the embedded and mobile market?
(including smartphones and tablets)
The ARM ISA is a RISC architecture, unlike the x86 ISA, which is of CISC type.
RISC ISAs operate as Load/Store architectures that use load and store instructions
to manage their register space but calculations are only performed with register
operands.
In contrast, CISC architectures allow specifying both register and memory
operands in calculations.
This has two consequences;
Due to their lower power consumption compared to CISC architectures, ARM
designs have become dominant in the embedded and mobile market (including
smartphones and tablets).
This is also the reason for the growing presence of ARM ISA-based server
and client processor designs.
CISC instructions are different long, ranging from 1 to 15 bytes.
This occurs because CISC instructions may involve memory operands.
In contrast, RISC instructions are equally long (typically 4-byte), as they only
refer to register operands (except LS instructions, which also can be encoded
in 4-bytes).
b) CISC architectures inherently consume more power because of memory fetches
and more complex decoding compared to RISC architectures.

## Slide 21: 1. Introduction to ARM (15)
ARM’s parent company is Acorn Computers (UK).
Acorn Computers began the Acorn RISC Machine project in October 1983
to develop a powerful processor for a line of business computers,
(two years after the introduction of the IBM PC).
The acronym ARM was originally coined at this time (1983) from the designation
Acorn RISC Machine.
In 1990, Advanced RISC Machines Ltd. (ARM Ltd.) was founded as a joint venture
of Acorn Computers, Apple Computers, and VLSI Technology.
Accordingly, the interpretation of ARM was altered to “Advanced RISC Machines”.
Historical remarks -1 [13], [14]

## Slide 22: 1. Introduction to ARM (16)
Figure: The headquarters of ARM Ltd. about 1990 [15]
Historical remarks -2

## Slide 23: 1. Introduction to ARM (17)
“ARM’s First Chip1 (from 1992)
Although the ARM processor were developed as a custom device for a highly specific purpose, the team designing it felt that the best way to produce a good custom solution was to produce a processor with good all-round performance. However, it’s interesting to note that the ARM’s architectural fate was sealed accidentally. While most of the RISC processor vendors were designing relatively huge chips (SPARC RISC, Intel i860, AMD 29000, etc.), ARM opted to develop a small-scale processor. One of the reasons the ARM processor was designed as a small-scale solution was that the resources to design it were not sufficient to allow the creation of a large and complex device. While this is now a technical plus for the ARM processor, it began as a necessity for a processor designed by a team of talented, but inexperienced designers (outside of university projects, most team members were programmers and board-level circuit designers) using new tools, some of which were far from state-of-the-art. Despite the unusal working quarters, the motivation and excitement of the small team was high and the company had an open, communicative style that helped maintain the “buzz”.
As with most start-up’s, ARM’s primary goal was to get the first product out; in this case, it was the ARM610, designed specifically for Apple. This product included full 32-bit addressing and endian-ness support, one of many changes requested by Apple in order to use the ARM processor in its planned products. An improved video controller, VIDC20, was also developed as well as a floating-point processor. Apple’s goal was to use the IP product within a hand-held personal organizer processor. The processor became known as ARM600, from which the 20 MHz ARM610 used in the Newton was later derived. At the same time, ARM Ltd.'s software team developed the ARM Cross Development Toolkit, a suite of software that allowed designers working on a range of platforms to use ARM development tools, assembler, compilers, and debugging and emulation programs.”
Optional reading: A brief account of the beginning of ARM [16]
1 Armv3 based

## Slide 24: 1. Introduction to ARM (18)
Finally, in 1998, the company went to the stock exchange and changed its name
to ARM Holdings plc, to its current designation.
Historical remarks -3

## Slide 25: 1. Introduction to ARM (19)
Historical remarks -4
Figure: ARM's recent headquarter in Cambridge (UK) [17]

## Slide 26: 1. Introduction to ARM (20)
Acquisition of ARM by Softbank (Japan)
It was completed in 2016.
Price: 31 bUSD (ARM's revenues in 2015 ≈ 1.5 bUSD).

## Slide 27: 1. Introduction to ARM (21)
NVIDIA’s intention to acquire ARM from Softbank
"The PC of the future will be made by new OEMs, sold through new distributors
and use a new instruction-set architecture.
ARM will be the most important CPU architecture of the future, and it already is
the fastest growing processor architecture.”
Announced in 09/2020
Price: 40 bUSD
To be completed in 2022.
NVIDIA’s aim was “burying x86 PCs,” as stated by their CEO (Huang) in 09/2020 [4]:
Remark
Considering the recent developments regarding the emergence and advantages of
ARM-based servers and DT processors, Huang’s vision seems to be not unfounded.

## Slide 28: 1. Introduction to ARM (22)
Cancellation of NVIDIA’s plan to acquire ARM [169]
In 02/2022 NVIDIA and Softbank (ARM’s owner) announced the termination of
the planned transaction due to regulatory objections.
On this occasion, Huang, CEO of NVIDIA, stated that “I expect (the) Arm (ISA)
to be the most important CPU architecture of the next decade.”,

## Slide 29
2. How has the Arm ISA evolved?
2.1 Overview of the evolution of the Arm ISA
2.2 A closer look at the SVE register set-based ISA extensions
2.3 Remarks on the evolution of Intel’s x86 ISA SIMD extension
(Sections 2.2 and 2.3 are optional readings and are not part of the Lecture.
Section 2.2 is included in the Annex.)

## Slide 30
2.1 Overview of the evolution of the Arm ISA

## Slide 31: 2.1 Overview of the evolution of the Arm ISA (1)
2.1 Overview of the evolution of the Arm ISA
Growth of instruction sets of processors over time [19]
Note in the above Figure that both RISC ISAs (Reduced Instruction Set Computer), such as
IBM’s PPC and the Arm ISA, as well as the x86 CISC (Complex Instruction Set Computer)
ISA evolve continuously.
The number of available instructions in both RISC and CISC ISAs has increased
to over 1000, resulting in a similar number of instructions for both.

## Slide 32: 2.1 Overview of the evolution of the Arm ISA (2)
Overview of ARM’s ISA versions
As previously mentioned, the ARM’s ISA has evolved enormously.
How huge work has been accomplished is indicated by the fact that the recent
(2022) Architecture Reference Manual [20] spans over 11000 pages.
A half-page excerpt of the manual illustrates this on the next slide.

## Slide 33: 2.1 Overview of the evolution of the Arm ISA (3)
Example: 1/2 page excerpt of the Arm Architecture Reference Manual (2022) [20]
(1/2 from 11530)

## Slide 34: 2.1 Overview of the evolution of the Arm ISA (4)
Arm ISA versions and the Arm basic ISA
Until now, there are nine major ISA versions, designated as Armv1 to Armv9,
(see the Figure below), which are described in the corresponding Architecture
Reference Manuals.
Armv4
Armv5
Armv6
Armv8.0-A
Armv7-A
ARM710T
(~1995)
ARM10200
(2000)
ARM1136
(2002)
Cortex-A5-A15
(2005)
Cortex-A55-75/X1
(2018)
Armv9-A
Neoverse N2/V1
Cortex-X2/A510/A710
cores (2021)
Armv3
ARM60
(1992)
Figure: Arm ISA versions
The earliest ISA versions (Armv1 (1985) and Armv2 (1987)) only provided an
address range of 26 bits yet.
These versions were owned by Acorn Computers Ltd, one of the vendors that
founded ARM in 1990.
The first ISA version with a 32-bit address range was the Armv3.
It was first implemented in the ARM60 processor in 1992 and was already owned
by ARM.
Therefore, we consider the Armv3 ISA as ARM’s basic ISA.
We will discuss its evolution next.

## Slide 35: 2.1 Overview of the evolution of the Arm ISA (5)
Key features of ARM’s basic ISA
Stack pointer
Link register
PC
Figure: Core registers in the Armv3-Armv7 ISA versions [21]
It is a simple 32-bit RISC ISA, intended för processing 32-bit scalar FX and
logical data, as its primary targets are microcontrollers.
This ISA provides 16 32-bit registers, known as the core registers.
13 of them are used as general-purpose registers (GPRs); while the remaining
three are dedicated, as shown below.
GPR

## Slide 36: 2.1 Overview of the evolution of the Arm ISA (6)
In which directions has ARM extended its basic ISA? (A simplified discussion)
Early focus of the Arm ISA extensions (1)
First ARM processors were often used in portable or embedded devices where code size
and the execution speed of bytecodes were crucial factors.
This motivated ARM to prioritize enhancements aimed at reducing code size and
speeding up the execution of bytecodes, as illustrated in the following Figure.
Main directions of extending ARM’s basic ISA
ISA extensions
to speed up
the execution of bytecodes
ISA extensions
to reduce
code size
After focusing on mobiles
these extensions became obsolete
Not discussed
Later, when Arm ISA-based processors transitioned to 64-bit, these extensions
became obsolete.

## Slide 37: 2.1 Overview of the evolution of the Arm ISA (7)
Changing focus of Arm ISA-based processors in the early 2000’s (2)
In the early 2000s, when Arm ISA-based processors became increasingly common
in mobile devices, more general workloads, including graphics processing,
became prevalent.
This is why, subsequently, ARM turned to enhancing compute capabilities through
FP and SIMD processing, as well as improving security, as indicated below.
ISA extensions
to enhance
compute capabilities
Main directions of extending ARM’s basic ISA
ISA extensions
to speed up
the execution of bytecodes
ISA extensions
to enhance
security
ISA extensions
to reduce
code size
Not discussed
Discussed
subsequently

## Slide 38: 2.1 Overview of the evolution of the Arm ISA (8)
Overview of the four main directions and introduced extensions of ARM’s basic ISA
(For the explanation of the superscripts in the Figure see the next slide)
Armv4
Armv5
Armv6
Armv8.0-A
Armv7-A
Jazelle
(Jazelle DBX)
VFPv1/2
Thumb6
(Armv4T)
SIMD
TrustZone
Thumb-2
(Armv6T2)
Adv. SIMD1
(NEON)
VFPv3/v42
Crypto-graph. extension
Jazelle
(ex. by SW)
Jazelle RCT3
(ThumbEE)
ARM710T
(~1995)
ARM10200
(2000)
ARM1136
(2002)
Cortex-A5 - A15
(2004)
Cortex-A53/A57
(2012)
To enhance
security
To speed up
the execution
of bytecodes
AArch32
AArch64
A32
AArch64
Armv9-A
Neoverse N2/V1
Cortex-X2/A510/A710
cores (2021)
A64
T32
(Thumb)
SVE4
(v8.2, opt.)
Confidential
Compute Arch.
MTE
A64
Aarch325
SVE2
To enhance
compute
capabilities
The thumb instruction set aims at reducing code size.

## Slide 39: 2.1 Overview of the evolution of the Arm ISA (9)
1Neon technology is ARM’s designation for Advanced SIMD extensions.
2 The VFP subset became deprecated in the Armv8 ISA.
3Jazelle-RTC (ThumbEE) became deprecated in Armv7 Issue C in 10/2011.
4The SVE (Scalable Vector Extension) subset was introduced in the Armv8.2
as an optional feature, only in 2017.
5The AArch32 execution mode is only supported in certain implementations, e.g.
in the Cortex-A510 CPU.
Explanation of the superscripts in the previous Figure

## Slide 40: 2.1 Overview of the evolution of the Arm ISA (10)
The most important extensions of the ARM ISA
In the long history of the evolution of the ARM ISA the most important releases were
a) the Armv7,
b) the Armv8.0
c) the Arm8.2 and
d) the Arm v9.0
ISAs.
Why is it so? We will discuss this next.

## Slide 41: 2.1 Overview of the evolution of the Arm ISA (11)
The Armv7 ISA release, announced in 2004, gave rise to the Cortex Family of CPU cores.
These CPU cores became the workhorse of mobile processors in the first decade
of the 2000’s.
a) The importance of the Armv7 ISA release

## Slide 42: 2.1 Overview of the evolution of the Arm ISA (12)
Overview of the Cortex family of CPU cores
In 10/2004, ARM announced the Cortex Family of CPU cores, along with its first model,
the Cortex-M3 CPU core.
The Cortex brand is used by ARM’s for their mobile application-oriented CPU cores,
which are based on the Armv7 ISA or later releases.
It is worth noting that ARM announced a second CPU brand in 2018 as well, called
Neoverse, to be used in processors focused on information infrastructures,
including datacenters, routers, switches, etc.), as discussed in another Chapter.

## Slide 43: 2.1 Overview of the evolution of the Arm ISA (13)
Profiles of ARM’s Cortex family of CPU cores [33], [34], [35] -1
The technical specification of the Armv7 ISA declared three family profiles to optimize
the Cortex family of CPU cores for specific market segments, as shown below.
Cortex-R profile
(Real-time profile)
Cortex-M profile
(Microcontroller profile)
Cortex-A profile
(Application profile)
Profiles of ARM’s Cortex family of CPU cores

## Slide 44: 2.1 Overview of the evolution of the Arm ISA (14)
Profiles of ARM’s Cortex family of CPU cores [33], [34], [35] -2
1) The Cortex-A (application) profile
It focuses on application processors that run mobile OSs and user applications, such as those found in smartphones, tablets, netbooks and eBook readers.
the 32-bit A32 and
the 16-bit T32 (which is a subset of the A32)
instruction sets.
At its introduction it supported two instruction sets:

## Slide 45: 2.1 Overview of the evolution of the Arm ISA (15)
2) The Cortex-M (Microcontroller) profile [35]
It supports writing interrupt handlers in high-level languages.
It is a variant of the T32 instruction set.
Profiles of ARM’s Cortex family of CPU cores [33], [34], [35] -3
CPUs of the M profile are optimized for embedded CPUs aimed at microcontroller
and cost-sensitive applications, such as IOT devices, smart sensors or simple
control tasks.

## Slide 46: 2.1 Overview of the evolution of the Arm ISA (16)
3) The Cortex-R (Real-time) profile [35]
It supports the A32 and T32 instruction sets.
Profiles of ARM’s Cortex family of CPU cores [33], [34], [35] -
It is designed for embedded CPUs to be used in real-time applications like
automotive control, robotics, avionics or industrial electronics systems.

## Slide 47: 2.1 Overview of the evolution of the Arm ISA (17)
Extending the ARM Cortex family with the SecurCore profile in 10/2007
Later, in 10/2007 ARM introduced the SecurCore profile.
It is optimized for smart card and secure applications.

## Slide 48: 2.1 Overview of the evolution of the Arm ISA (18)
Overview of
Cortex profiles
and related CPU cores
(as of 2017) [33]

## Slide 49: 2.1 Overview of the evolution of the Arm ISA (19)
According to the general scope of this Lecture Notes, subsequently, we will only focus
on the Cortex-A series of CPU cores.
Remark

## Slide 50: 2.1 Overview of the evolution of the Arm ISA (20)
Introducing a secondary register set into the Armv7 ISA and implementing it
in the CPU core
Figure: Introducing a secondary register set into the Armv7 ISA,
which was implemented in the CPU core
64
32
Armv7 (or Armv8 AArch32 mode)
(2004)
(Implemented in
the CPU core)
Following the graphics needs of the already widely used ARM-based mobile devices,
the company introduced a secondary register set of 32 x 64 bits, which was
implemented in the CPU core, as illustrated below.

## Slide 51: 2.1 Overview of the evolution of the Arm ISA (21)
Remark
Figure: Introducing a secondary register set into the ISA of the FP coprocessor
defined in Armv5 and extending and relocating it into the CPU core in the Armv7 ISA
32
64
32
32
Armv5
Armv7
(2000)
(2004)
(Implemented in
the coprocessor)
(Implemented in
the CPU core)
Before the Armv5 release, the Arm ISA did not support FP calculations.
The Armv5 ISA was then enhanced to support such calculations by assuming the
presence of an FP coprocessor, which was particularly beneficial for applications
such as 3D graphics.
In this setup, the FP calculations were offloaded to the FP coprocessor, which
performed the necessary operations and then returned their results to the CPU core.
To facilitate the FP calculations, the ISA of the FP coprocessor provided a secondary
register set consisting of 32 registers, each 64 bits in size, as indicated in the Figure below.
Later, the Armv7 release already supported FP calculations directly in the CPU core, therefore,
the secondary register space was relocated into the CPU core, and it became extended.

## Slide 52: 2.1 Overview of the evolution of the Arm ISA (22)
In the Armv8.0 ISA revision in 2012, ARM opened the way for 64-bit processing and
largely extended the register spaces available for computing, as discussed later.
The new 64-bit Armv8.0 ISA introduced two execution modes (AArch32/Aarch64)
in order to ensure backward compatibility with the 32-bit Armv7 ISA.
In the Aarch32 execution mode, processors behave like Armv7 processors, with
the same execution capabilities as provided in the Armv7 ISA.
In the Aarch64 execution mode, the processor has a largely extended register space
for executing instructions, compared to the Armv7 ISA, as discussed later.
At the same time, early aspects, such as reducing code size and speeding up the
execution of bytecodes became irrelevant and their support was dropped,
as indicated in the related Figure.
b) The importance of the Armv8.0 ISA release

## Slide 53: 2.1 Overview of the evolution of the Arm ISA (23)
1) Extending the GPR register set in the Armv8 ISA [21], [22]
32-bit wide
32-bit wide
64-bit wide
32-bit access
64-bit access
GPRs in the Armv8 ISA
in the AArch64 execution mode (2012)
GPRs in the Armv3-Armv7 ISA
and in the Armv8 ISA
in the AArch32 execution mode (2012)
Dedicated use
Dedicated use
Stack pointer
Link register
PC
R0
R1
R2
.
.
.
R12
R13(SP)
R14(LR)
R15(PC)
X0
X1
X2
.
.
.
X12
X13
X14
.
.
.
X30
X31
X3
W0
W1
W2
.
.
.
W12
W13
W14
.
.
.
W30
W31
W3
The GPR register set was vastly enlarged in the Armv8 ISA in the AArch64 mode (see below).

## Slide 54: 2.1 Overview of the evolution of the Arm ISA (24)
2) Extending the secondary register set in the Armv8 ISA
Figure: Introducing a secondary register set into the Arm ISA and its evolution
32
64
128
32
32
32
Armv5
Armv7 (or Armv8 AArch32 mode)
Armv8 AArch64 mode
(2000)
(2004)
(2012)
(Implemented in
the coprocessor)
(Implemented in
the CPU core)
(Implemented in
the CPU core)
In the Armv8 Aarch64 execution mode, ARM widened the secondary register set to
32 x 128-bit in 2012, as illustrated below, to provide better support for 128-bit processing.

## Slide 55: 2.1 Overview of the evolution of the Arm ISA (25)
c) The importance of the Armv8.2 ISA release
The next major release was the Armv8.2 ISA, which was introduced in 04/2012.
(It was not indicated in the Figure summarizing the evolution of the ARM ISA
due to space limitations).
It introduced the SVE (Scalable Vector Extension), further on various data formats
and instructions to support AI computations, such as half-precision FP or Bfloat,
(not discussed in the Lecture).
These extensions were initially optional but became mandatory later in Armv9
ISA releases.
The SVE extension has great importance since it allows
1) very wide (up to 16x128-bit) vector (i.e. SMD) processing and
2( vector length agnostic programming (to be discussed later in this Section)

## Slide 56: 2.1 Overview of the evolution of the Arm ISA (26)
1) How was very wide (up to 16x128-bit) vector (SMD) processing implemented?
To implement very wide vector processing ARM introduced a third register set,
referred to as the SVE (Scalable Vector Extension) register set into the Armv8 ISA,
as follows:
128
32
SVE register set
---
(1...16) x 128 bit
Figure: The SVE register set
In Armv8.2 (AArch64 mode)
SVE is designed for HPC (i.e. scientific) workloads rather than media or image
processing.
It provides 32 registers (referred to as Z0 – Z31), each capable of holding
up to 16 x 128-bit long data (implementation dependent), as seen below.
SVE supports both FX- and FP SIMD operationsg.
The SVE ISA extension is only implemented in the AArch64 mode.

## Slide 57: 2.1 Overview of the evolution of the Arm ISA (27)
Vector-length agnostic programming means that the same program code can be
written and run on processors with different wide execution units, such as
on processors with 128- or 256- or 512-bit wide SIMD FX/FP units.
In SVE programming, the available execution width of the processor is specified
in a register, and the program execution will be adjusted accordingly.
The benefit of vector-length agnostic programming
Its benefit is that the binary code is portable across different processors with varying
wide SIMD execution units, as illustrated below and explained in Section 2.4.
Figure: The benefit of SVE programming: vector-length agnostic programming
2) What does vector length agnostic programming mean?

## Slide 58: 2.1 Overview of the evolution of the Arm ISA (28)
d) The importance of the Armv9.0 ISA release
The last phase of the ISA evolution, revealed in 03/2021, is connected to the
Armv9.0 release.
The Armv9.0 release made SVE mandatory while it was optional in Armv8.2 from
2017 onwards.
Additionally, Armv9.0 introduced SVE2 as a mandatory feature.
SVE2 is a superset of SVE and the SIMD oriented Neon.
It aims at replacing Neon.
It allows writing binary portable programs for a wide range of applications,
as described in Section 2.4.
To enhance security, Armv9.0 also introduced the Confidential Compute Architecture
concept and Memory Tagging as well, with only the latter being discussed
in Section 3.6 c.

## Slide 59
2.1 Overview of the evolution of the Arm ISA (29)
New instruction types introduced in the Arm ISA extensions to enhance compute capabilities
GPR reg. set based
Secondary register set basedt
SVE register set based
FX SIMD
extensions
Vector FP
extension
FX/FP SIMD
extensions
Scalar FP
extensions
Very long FX/FP SIMD
extensions
(Coproc. based)
(Coproc. based)
(Sequentially executed)
(64/128-bit)
(128-2048-bit)
(Neon)
(SVE/SVE2)
Evolution of the instruction types introduced in the subsequent ISA releases
to enhance compute capabilities -1
Armv6
(2002)
Armv5
(2000)
Armv5
(2000)
64-bit:Armv7
(2004)
128-bit: Armv8.0 (2012)
SVE: Armv8.2 (opt.) (2017)
SVE2: Armv9 (mandatory) (2021)
Introduced in
The GPR register set-based FX SIMD extensions were integrated into the
secondary register set-based FX/FP SIMD extensions.
The coprocessor-based extensions soon became obsolete.
Remarks

## Slide 60: 2.1 Overview of the evolution of the Arm ISA (30)
Evolution of the instruction types introduced in the subsequent ISA releases
to enhance compute capabilities -2
The previous Figure indicates the evolution of the computing capabilities of the
ARM ISA.
It began by introducing scalar FP and vector FP support through a coprocessor.
This was later followed by adding the support of 32-bit FX-SIMD, 64/128-bit
FX/FP-SIMD and eventually 128 to 2024-bit FX/FP SIMD instructions.
These enhancements were provided to improve computational capabilities for
emerging new applications, starting with basic mobile applications, subsequently
for multimedia and 3D graphics, and ultimately addressing high-performance (HP)
computing and AI applications.

## Slide 61
2.1 Overview of the evolution of the Arm ISA (31)
Which Arm ISA extensions are used at present in numeric computations?
From all extensions introduced for enhancing the compute capabilities of the Arm ISA,
recently, only
Arm ISA extensions introduced to enhance compute capabilities
GPR reg. set
Secondary register set
SVE register set
FX SIMD
extensions
Vector FP
extension
FX/FP SIMD
extensions
Scalar FP
extensions
Very long FX/FP SIMD
extensions
(Co-proc. based)
(Co-proc. based)
(Sequentially executed)
(Neon)
v7: (64-bit) (2004)
v8.0: (128-bit) (2012)
(128-2048-bit)
v8.2: SVE (2017)
v9: SVE2 (2021)
the 128-bit FX/FP SIMD extension (commonly called Neon) and
the 128-2028-bit long FX/FP SIMD extensions, called SVE/SVE2
are of importance, they absorb all previous extensions.

## Slide 62
2.2 A closer look at the SVE register set-based ISA extensions
(Optional reading, it is included in the Annex).

## Slide 63
2.3 Remarks to the evolution of Intel’s x86 ISA SIMD extensions
(Optional reading).

## Slide 64: 2.3 Remarks to the evolution of Intel’s x86 ISA SIMD extensions (1)
It is worth comparing the evolution of SIMD extensions provided by the x86 ISA with
those introduced by the Arm ISA.
Intel introduced their first multimedia-inspired MMX extension in the Pentium M
processor in 1997 utilizing the 64-bit mantissa part of the FP registers.
Subsequently, Intel introduced a dedicated SIMD register space in the SSE extension
in the Pentium III (Katmai) core in 1999, as shown in the next Figure.
Remarks to the evolution of Intel’s x86 ISA SIMD extensions [23] -1

## Slide 65: 2.3 Remarks to the evolution of Intel’s x86 ISA SIMD extensions (2)
AVX-512
(xmm0-xmm31)
SSE (32-bit)
(xmm0-xmm7)
AVX/AVX2
ymm0-ymm15)
AVX-512
(ymm0-ymm31
AVX-512
(zmm0-zmm31
0
7
15
31
xmm (128-0)
ymm (255-0)
zmm (511-0)
0
127
255
511
Figure: The x86 ISA’s dedicated register space for SIMD processing and its extensions [24]
The introduced SIMD register space was initially 8x128-bit in size.
It was later extended in three steps, as shown below.
first to 16x128-bit (in the SSE3 extension, in 2004),
then to 16x256-bit (in the AVX extension, in 2011) and
finally, to 32x512-bit (in the AVX512 extension, in 2017).
The extension was implemented in an aliased manner, as discussed next.
SSE2(64-bit)
(xmm0-xmm15)
Remarks to the evolution of Intel’s x86 ISA SIMD extensions [23] -2

## Slide 66: 2.3 Remarks to the evolution of Intel’s x86 ISA SIMD extensions (3)
Remark
In an aliased extension the lower parts of the extended registers (e.g. 256-bit registers)
are the preceding (e.g. 128-bit) registers, as illustrated below.
Figure: Extending the existing 128-bit wide XMM [0, 15] SIMD register set
to the 256-bit YMM [0, 15] register set in an aliased way [25]

## Slide 67: 2.3 Remarks to the evolution of Intel’s x86 ISA SIMD extensions (4)
PII
Klamath,
(1997)
Pentium_MMX
(1997)
Core
Cannon-Lake,
(2018)
Skylake-X/SP,
(2017)
(2016)
Overview of Intel’s x86 ISA SIMD extensions [23]
Based on the register space extensions Intel
introduced the following SIMD extensions
of the x86 ISA:

## Slide 68: 2.3 Remarks to the evolution of Intel’s x86 ISA SIMD extensions (5)
SSE SIMD extensions
SIMD extensions of Intel’s x86 ISA
AVX-512
SIMD extension
AVX2 SIMD extension
128-bit
FX/FP SIMD
(FP32)
256-bit
FX/FP SIMD
(FP32/FP64)
512-bit
FX/FP SIMD
(FP32/FP64)
MMX SIMD
extensions
64-bit
FX SIMD
(Pentium-MMX)
(1997)
(Pentium III)
(1999)
(Haswell
(2013)
(Cannon Lake)
(2018)
Introduced in
DTs/laptops
AVX SIMD extension
256-bit
FP SIMD
(FP32/FP64)
(Sandy Bridge)
(2011)
SSE2, SSE4.2 SIMD extensions
128-bit
FX/FP SIMD
(FP32/FP64)
(Pentium 4
Willamette)
(2000)
Summing up Intel’s x86 ISA SIMD extensions [23]
xmm0..7
xmm0..15
ymm0..15
ymm0..15
zmm0..15
Register names

## Slide 69: 2.3 Remarks to the evolution of Intel’s x86 ISA SIMD extensions (6)
Comparing Intel’s and AMD’s recent SIMD extensions -1
In addition to the existing general-purpose 16x64-bit GPR and 8x80-bit FP architectural
register sets, Intel introduced three dedicated register sets in succession for SIMD
processing with 16x128-, 16x256- and 32x512-bit registers into their x86-64 ISA.
The extended registers are aliased, meaning that the shorter registers are used as the
lower parts of the extended registers.
It is important to note that Intel introduced a new set of instructions for each extension.
In contrast, for SIMD processing, ARM introduced two additional distinct register sets;
an up to 32x128-bit secondary register set for the Neon (SIMD) extension and a
32x128 to 32x2048-bit SVE register set for the SVE/SVE2 instruction extensions.

## Slide 70: 2.3 Remarks to the evolution of Intel’s x86 ISA SIMD extensions (7)
Comparing Intel’s and AMD’s recent SIMD extensions -2
As we discussed, both the x86 and Arm ISAs support increasingly wider SIMD
execution, such as 64-bit, 128-bit, 256-bit, and 512-bit long SIMD processing.
However, with the x86 ISA, each new extension, such as MMX, SSE, SSE2, SSE3,
AVX, AVX512, a further subset of instructions is introduced.
This evolution path has a drawback because to take advantage of the wider and
wider SIMD execution resources, software had to be rewritten and recompiled.
By contrast, with the SVE extension of the Arm ISA, programming becomes
"vector length agnostic," meaning the programmer no longer needs to use
different instruction subsets for different long ISA extensions.

## Slide 71
3. How have ARM’s CPU core designs evolved over time?
3.1 ARM’s CPU designs preceding the ARM Cortex family
3.2 Overview of the Cortex family of CPU cores
3.4 Armv8.0-A ISA-based 64-bit Cortex-A CPUs
3.3 Armv7-A ISA-based 32-bit Cortex-A CPUs
3.5 Armv8.2-A ISA-based 64-bit Cortex-A CPUs
3.6 Armv9-A based 64-bit Cortex-A CPUs
3.7 Case example: The core complex of the TCS22 platform
3.8 Summing up: Main evolution steps of Armv7 to
Armv9-based CPU designs in mobile processors
(Sections 3.1 and 3.7 are optional readings; they are not part of the Lecture.
These Sections are included in the Annex.)

## Slide 72: 3. How have ARM’s CPU designs evolved? (1)
3. How have ARM’s CPU designs evolved over time?
Overview of ARM’s CPU core designs
ARM1-ARM3
26-bit address bus
32-bit data buses
ARM6xx-ARM11xx
32-bit address bus
32-bit data buses
Target infrastructure
(servers, edge)
Mainly target mobiles,
though several vendors
entered the market with
Arm ISA-based client or
server designs as well.
Section 3.1
Sections 3.2-3.7
Optional reading,
is not part of the exam.
CPU cores based on the Armv1–v2 ISA
(Earliest ARM cores)
(~ 1985-1990)
CPU cores based on
the Armv3–v6 ISA
(Early ARM cores)
(~ 1992-2004)
CPU cores based on
the Armv7 – Armv9 ISA
CPU cores based on
the Armv9 ISA
Since 2021
Since 2004
ARM’s early CPU cores
ARM’s CPU core designs
ARM’s Cortex-A
CPU cores
ARM’s Neoverse
CPU cores
Optional reading,
not part of the exam.

## Slide 73: 3. How have ARM’s CPU designs evolved? (2)
Overview of Armv7- to Armv9-based Cortex-A CPU designs
Section 3.3
Section 3.5
Section 3.6
Cortex-A8
Cortex-A57/A53
Cortex-A75/A55
Cortex-X2/A710/A510
First CPUs
Section 3.4
based on
the 32-bit Armv7-A ISA
Cortex-A CPUs
based on
the Armv8.0-A ISA
based on
the Armv8.2-A ISA
based on
the Armv9-A ISA
(Please note that from Section 3, only Subsections 3.3.4 (big.little CPUs) and 3.6
(Armv9-A ISA-based CPUs) are included in the Lecture and the exam.

## Slide 74
3.1 ARM’s CPU designs preceding the ARM Cortex family
(Optional reading, not part of the Lecture.
It is included in the Annex.)

## Slide 75
3.2 Overview of the Cortex family of CPU cores

## Slide 76: 3.2 Overview of the Cortex family of CPU cores (1)
3.2 Overview of the Cortex family of CPU cores
In 10/2004, ARM announced the Cortex Family of CPU cores, along with its first model,
the Cortex-M3 CPU core.
The Cortex brand is used by ARM’s for their mobile application-oriented CPU cores,
which are based on the Armv7 ISA or later releases.
It is worth noting that ARM announced a second CPU brand in 2018 as well, called
Neoverse, to be used in processors focused on information infrastructures,
including datacenters, routers, switches, etc.), as discussed in another Chapter.

## Slide 77: 3.2 Overview of the Cortex family of CPU cores (2)
Profiles of ARM’s Cortex family of CPU cores [33], [34], [35] -1
The technical specification of the Armv7 ISA declared three family profiles to optimize
the Cortex family of CPU cores for specific market segments, as shown below.
Cortex-R profile
(Real-time profile)
Cortex-M profile
(Microcontroller profile)
Cortex-A profile
(Application profile)
Profiles of ARM’s Cortex family of CPU cores

## Slide 78: 3.2 Overview of the Cortex family of CPU cores (3)
Profiles of ARM’s Cortex family of CPU cores [33], [34], [35] -2
a) The Cortex-A (application) profile
It targets application processors that run mobile OSs and user applications, such as
processors in smartphones, tablets, netbooks and eBook readers.
the AArch32 execution mode to maintain compatibility with the A32
instruction set and
the AArch64 execution modes, to allow using the new, 64-bit A64
instruction set.
At the same time, in the AArch64 mode ARM terminated the support
of the T32 (Thumb) instruction set.
that supports 64-bit processing and has two execution modes:
the 32-bit A32 and
the 16-bit T32 (which is a subset of the A32)
instruction sets.
At its introduction it supported two instruction sets:
Finally, in the Armv9.0-A ISA, which was released in 2021
ARM has withdrawn the general availability of the AArch32 execution mode,
as indicated in the next Figure.
Later, in 2012, the Armv8-A ISA was released

## Slide 79: 3.2 Overview of the Cortex family of CPU cores (4)
Overview of the Cortex CPUs
Armv4
Armv5
Armv6
Armv8.0-A
Armv7-A
Jazelle
(Jazelle DBX)
VFPv1/2
Thumb6
(Armv4T)
SIMD
TrustZone
Thumb-2
(Armv6T2)
Adv. SIMD1
(NEON)
VFPv3/v42
Crypto-graph. extension
Jazelle
(ex. by SW)
Jazelle RCT3
(ThumbEE)
ARM710T
(~1995)
ARM10200
(2000)
ARM1136
(2002)
Cortex-A5 - A15
(2005)
Cortex-A53/A57
(2012)
To enhance
security
To speed up
the execution
of bytecodes
AArch32
AArch64
A32
AArch64
Armv9-A
Neoverse N2/V1
Cortex-X2/A510/A710
(2021)
A64
T32
(Thumb)
SVE4
(v8.2, opt.)
Confidential
Compute Arch.
MTE
A64
Aarch325
SVE2
To enhance
compute
capabilities
For the Remarks see the next slide.

## Slide 80: 3.2 Overview of the Cortex family of CPU cores (5)
1The Advanced SIMD architecture extension is commonly referred to as the
NEON technology.
The VFP subset became depricated in the Armv8 ISA.
3Jazelle-RTC (ThumbEE) became depricated in Armv7 Issue C in 10/2011.
4The SVE (Scalable Vector Extension) subset became introduced in the
Armv8 ISA as an optional feature, only in 2017.
5The AArch32 execution mode is only supported in certain implementations, e.g.
in the Cortex-A510 CPU.
6 The Thumb extension aims at reducing code size.
Remarks to the introduced extensions

## Slide 81: 3.2 Overview of the Cortex family of CPU cores (6)
c) The Cortex-R (Real-time) profile [35]
b) The Cortex-M (Microcontroller) profile [35]
It supports the A32 and T32 instruction sets.
It supports writing interrupt handlers in high-level languages.
It is a variant of the T32 instruction set.
Profiles of ARM’s Cortex family of CPU cores [33], [34], [35] -3
CPUs of the M profile are optimized for embedded CPUs aimed at microcontroller
and cost-sensitive applications, such as IOT devices, smart sensors or simple
control tasks.
It is designed for embedded CPUs to be used in real-time applications like
automotive control, robotics, avionics or industrial electronics systems.

## Slide 82: 3.2 Overview of the Cortex family of CPU cores (7)
Extending the ARM Cortex family with the SecurCore profile in 10/2007
In 10/2007 ARM introduced the SecurCore profile.
It is optimized for smart card and secure applications.

## Slide 83: 3.2 Overview of the Cortex family of CPU cores (8)
Overview of
Cortex profiles
and related CPU cores
(as of 2015) [33]

## Slide 84: 3.2 Overview of the Cortex family of CPU cores (9)
According to the general scope of this Lecture Notes, subsequently, we will only focus
on the Cortex-A series of CPU cores.
Remark

## Slide 85: 3.2 Overview of the Cortex family of CPU cores (10)
Evolution of the Cortex-A family of CPUs
Overview
based on
the 32-bit Armv7-A ISA
Cortex-A CPUs
based on
the Armv8.0-A ISA
based on
the Armv8.2-A ISA
based on
the Armv9-A ISA

## Slide 86
3.3 Armv7-A ISA-based 32-bit Cortex-A CPUs
3.3.1 Overview of Armv7-based 32-bit CPU designs
3.3.2 Armv7-based 32-bit single-core CPUs
3.3.4 Armv7-based 32-bit big.little CPUs
3.3.3 Armv7-based 32-bit symmetrical multicore CPUs
(Only Subsections 3.3.3 and 3.3.4 are part of Lecture and the exam; further parts are optional.
Notes: 86

## Slide 87
3.3.1 Overview of Armv7-based 32-bit CPU designs
Notes: 87

## Slide 88: 3.3.1 Overview of Armv7-based 32-bit CPU designs (1)
3.3.1 Overview of Armv7-based 32-bit Cortex-A CPU designs
Section 3.3
Section 3.5
Section 3.6
Cortex-A8
Cortex-A57/A53
Cortex-A75/A55
Cortex-X2/A710/A510
First CPUs
Section 3.4
based on
the 32-bit Armv7-A ISA
Cortex-A CPUs
based on
the Armv8.0-A ISA
based on
the Armv8.2-A ISA
based on
the Armv9-A ISA

## Slide 89: 3.3.1 Overview of Armv7-based 32-bit CPU designs (2)
Overview of Armv7-A ISA-based 32-bit Cortex-A CPUs (based on [36]) -2
2012
2013
10/2009
Cortex-A5
Armv7
40 nm
High Performance
Mainstream
Low power
Announced
1
2
3
4
5
2006
2007
2008
2009
2010
2011
10/2011
Cortex-A7
Armv7
28 nm
10/2012
Cortex-A53
Armv8
20/16 nm
10/2005
Cortex-A8
Armv7
65 nm
10/2007
Cortex-A9
Armv7
40 nm
9/2010
Cortex-A15
Armv7
32/28 nm
10/2012
Cortex-A57
Armv8
20/16 nm
2014
2/2014
Cortex-A17
Armv7
28 nm
6
7
DMIPS/MHz
2015
2/2015
Cortex-A72
Armv8
16 nm
11/2015
Cortex-A35
Armv8
16/14 nm
8
2016
5/2016
Cortex-A73
Armv8
10 nm
6/2013
Cortex-A12
Armv7
28 nm
Armv7-A
(32-bit)
Armv8.0-A
(64-bit)
(Dhrystone MIPS: relative performance of the
DEC VAX 11/780 minicomputer)
(Dhrystone: synthetic benchmark for syst. progr.)

## Slide 90
CPU Core | Announced | Available in devices | Target category | L2 cache | Multicore support (MPCore) | big.LITTLE support | Efficiency DMIPS/MHZ
Cortex-A8 | 2005 | 2009 | Mainstream | Optional | No | -- | 2,0
Cortex-A9 | 2007 | 2010 | Mainstream | Optional | Yes | -- | 2,5
Cortex-A5 | 2009 | 2011 | Low power | No L2 | Yes | -- | 1,6
Cortex-A15 | 2010 | Q2/2013 | High-end | Mandatory | Yes | Yes (with A7) | 4,0
Cortex-A7 | 2011 | 2012 | Low power | Optional | Yes | Yes (A15/A17) | 1,9
(Cortex-A12) | 2013 | withdrawn | Mainstream | -- | Yes | -- | 3,0
Cortex-A17 | 2014 | 2015 | Mainstream | Mandatory | Yes | Yes (with A7) | 4,0
Main features of Armv7 ISA-based Cortex-A CPUs [37]
3.3.1 Overview of Armv7-based 32-bit CPU designs (3)
Note that initially, Armv7-based Cortex-A CPUs had an optional L2 cache.
The L2 cache became mandatory in the big cores of big.little architetures, while
the low-power (high-efficiency) A5 CPU core did not include an L2 cache.
Other features will be discussed later.

## Slide 91: 3.3.1 Overview of Armv7-based 32-bit CPU designs (4)
Evolution of the CPU designs in Armv7-based 32-bit mobile processors
Symmetrical multicore
CPUs
big-little
CPUs
Single-core
CPUs
Armv7-based 32-bit CPU designs in mobile processors
CC interconnect
CC interconnect
(~2011-2013)
(~2013-2016)
(≈2007-2012)
Cortex-A5/A9
Cortex-A7/A15/A17
Cortex-A8
Typical Armv7 CPUs
(3.3.2)
(3.3.3)
(3.3.4)
As seen above, over time, single-core Armv7-based 32-bit CPUs advanced to
symmetrical multicores and then to big.little designs, as will be discussed subsequently.

## Slide 92
3.3.2 Armv7-based 32-bit single-core CPUs
Notes: 92

## Slide 93: 3.3.2 Armv7-based 32-bit single-core CPUs (1)
3.3.2 Armv7-based 32-bit single-core CPUs
Symmetrical multicore
CPUs
big-little
CPUs
Single-core
CPUs
Armv7-based 32-bit CPU designs in mobile processors
CC interconnect
CC interconnect
(~2011-2013)
(~2013-2016)
(≈2007-2012)
Cortex-A5/A9
Cortex-A7/A15/A17
Cortex-A8
Typical Armv7 CPUs

## Slide 94: 3.3.2 Armv7-based 32-bit single-core CPUs (2)
Use of Armv7-based 32-bit CPUs in single core mobile processors -1
Symmetrical
multicores
bit big-little
core clusters
Single-core
processors
Armv7-based 32-bit CPU designs in mobile processors
Cortex-A5/A9
HP: Cortex-A15/A17
LP: Cortex-A7
Armv7-A
CPUs
Cortex-A8
A5 (2011)
(2C)
Apple
4412 4C (2012)
7 7580 2x4C (2015)
5410 (4+4)C (2013)
5420 (4+4)C (2013)
Samsung
Exynos
8260 2C (2013)
400 4C (2013)
Qualcomm
Snapdragon
Huawei
Kirin
920 (4+4)) 2014)
(K3V2 4C (2012)
620 2x4C (2014)
MediaTek
MT6582 4C (2013)
MT6592 2x4C (2013)
MT8135 (2+2)C (2013)
MT6595 (4+4)C (2014)
APL2298 1C (2009)
QSD8250 1C (2007)
(A8-based Scorpion core)
3110 1C (2010)
CC interconnect
CC interconnect
MT6515 1C (2012)
MT6575 1C (2012)

## Slide 95: 3.3.2 Armv7-based 32-bit single-core CPUs (3)
Use of Armv7-based 32-bit CPUs in single core mobile processors -2
As the precious Figure shows, Armv7-based single-core processors emerged
between 2007 and 2012 and were mostly built on the Cortex-A8 core.
The L2 cache was an optional feature yet.

## Slide 96
3.3.3 Armv7-based 32-bit symmetrical multicore CPUs
This Subsection is part of the Lecture and the exam.
Notes: 96

## Slide 97: 3.3.3 Armv7-based 32-bit symmetrical multicore CPUs (1)
Symmetrical multicore
CPUs
big-little
CPUs
Single-core
CPUs
Armv7-based 32-bit CPU designs in mobile processors
3.3.3 Armv7-based 32-bit symmetrical multicore CPUs
CC interconnect
CC interconnect
(~2011-2013)
(~2013-2016)
(≈2007-2012)
Cortex-A5/A9
Cortex-A7/A15/A17
Cortex-A8
Typical Armv7 CPUs

## Slide 98: 3.3.3 Armv7-based 32-bit symmetrical multicore CPUs (2)
Their goal is to raise performance by utilizing multiple CPU cores for execution
(rather than increasing reliability by using multiple cores).
Aim of introducing symmetrical multicores

## Slide 99: 3.3.3 Armv7-based 32-bit symmetrical multicore CPUs (3)
Symmetrical multicores
built up of individual cores
Symmetrical multicores
built up of core blocks
Ci
Ci
Ci
Ci
Shared, segmented L2
Interconnection network (e.g. Crossbar)
Ci
Ci
Ci
Ci
Shared, segmented L2
Implementation alternatives of symmetrical multicores
(regarding the use of core blocks)
Cores are grouped into core blocks,
each with shared L2 or L3 caches, and
each core block is linked to the
Interconnection network via separate links.
Cores with or without shared L2 or l3 caches
are treated as individual units and
each core is linked to the
Interconnection network via private links.
ARM’s approach
Intel’s approach
Examples
Armv6-based ARM11 MPCore (2004)
Armv7/v8-based symmetrical multicores
(2004 ~ 2013)
Intel’s Core-based processors from the 1st gen.
Core 2 line (2006) up to the 11th gen Raptor Lake (2021)
Interconnection network (e.g. Ring bus)

## Slide 100: 3.3.3 Armv7-based 32-bit symmetrical multicore CPUs (4)
Example
Figure: Example of a symmetrical multicore processor [38]
(actually, Samsung’s Exynos 4412 mobile processor, 2012)
Armv7-based 32-bit core-blocks based symmetrical multicore CPUs
Such CPUs are typically organized in a 4-core block, operating in parallel, supported
by a shared L2 cache and interconnected with a common link to the system
interconnect, like the cores in the Figure below.

## Slide 101: 3.3.3 Armv7-based 32-bit symmetrical multicore CPUs (5)
A5 (2011)
(2C)
Apple
4412 4C (2012)
Samsung
Exynos
8260 2C (2013)
400 4C (2013)
Qualcomm
Snapdragon
Huawei
Kirin
(K3V2 4C (2012)
MediaTek
MT6582 4C (2013)
MT6592 2x4C (2013)
Cortex-A5/A9
ARM
Cortex-A8
APL2298 1C (2009)
QSD8250 1C (2007)
(A8-based Scorpion core)
3110 1C (2010)
When did Armv7-based 32-bit symmetrical multicore CPUs emerge
in mobile processors?
Below, we show how single-core processors transitioned to Armv7-based symmetrical multicores.
Single-core processors
Symmetrical multi-core processors
As the above Figure indicates, Armv7-based symmetrical multicores replaced
single-core designs in mobile processors in the early 2010s.
This shift occurred about five years later than in desktop processors since the first
dual-core desktop processors first appeared around 2005, such as Intel’s Pentium D (2005),
Core 2 (2006) or AMD’s K8-based Toledo (2005).
MT6515 1C (2012)
MT6575 1C (2012)

## Slide 102: 3.3.3 Armv7-based 32-bit symmetrical multicore CPUs (6)
3-cores
8-cores
2-cores
4-cores
Core counts in Armv7-based 32-bit mobile processors with symmetrical multicores
Apple
Samsung
Exynos
Qualcomm
Snapdragon
Huawei
Kirin
MediaTek
A5 (2011)
(2x Cortex-A9)
A7 (2013)
(2x 64-bit Cyclone)
Exynos 4412 (2012)
4x Cortex-A9
Exynos 3250 (2011)
2x Cortex-A7
S400 (2013)
4x Cortex-A7
S200 (2013)
2x Cortex-A7
K3V2 (2012)
(4x Cortex-A9)
MT6582 (2013)
4x Cortex-A7
MT6592 (2013)
2x4 Cortex-A7
MT6572 (2013)
2x Cortex-A7
Evolution of core counts in Armv7-based 32-bit symmetrical multicores
in mobile processors
After the model designations, we indicate the release dates of the first models of the related lines
with the number of cores.
First symmetrical multicores were typically dual core CPUs, but soon they became enhanced
to higher core counts, as seen below.

## Slide 103: 3.3.3 Armv7-based 32-bit symmetrical multicore CPUs (7)
Typical implementations of Armv7-based symmetrical multicores -1
a) Implementation of Armv7-based dual- and quad-core-core symmetrical multicores
4-way core cluster with shared L2
2-way core cluster with shared L2
C0
C0
C0
C0
L1I/L1D
L1I/L1D
L1I/L1D
L1I/L1D
L2
L2
C0
C0
L1I/L1D
L2
L2
L1I/L1D
Armv7-based dual- and quad-core symmetrical CPUs are built with private L1 caches
and a shared (inclusive) L2 cache, as shown below:
By contrast, Armv7-based octa-core processors including the same type of cores
(i.e., homogeneous multicores) have a different implementation, as discussed next.
Examples
Apple’s A5 (2011)
(Based on 2xCortex-A9)
Samsung 4412 (2012)
(Based on 4xCortex-A9)

## Slide 104: 3.3.3 Armv7-based 32-bit symmetrical multicore CPUs (8)
Typical implementations of Armv7-based symmetrical multicores -2
b) Implementation of Armv7-based octa-core symmetrical multicores
Armv7-based octa-core CPUs with identical core types are implemented as
dual, quad-core core blocks (clusters), with an L2 cache shared by all four cores
of the core block, as depicted in the Figure below.
Ci
Ci
Ci
Ci
Shared, segmented L2
Interconnection Network (e.g. Crossbar)
Ci
Ci
Ci
Ci
Shared, segmented L2
Figure: Implementation of Armv7-based octa-core CPUs including the same type of cores
Octa-core CPU implemented
as dual quad-core core blocks
E.g. 32-bit MediaTek’s MT6592 (2013)
Huawei’s Kirin 620 (2014)
Samsung’s Exynos 7 7580 (2015)

## Slide 105: 3.3.3 Armv7-based 32-bit symmetrical multicore CPUs (9)
Figure: Intel’s 10th gen. Comet Lake processor built up as a homogeneous
symmetrical multicore [39]
Cache-coherent ring bus
The CPU is designed differently from AMD’s Zen-based or Armv7-based homogeneous
symmetrical multicore designs.
Each core has its own L2 cache and L3 cache segment and is individually linked
to the system interconnect.
Intel’s subsequent 12th gen. Alder Lake family introduced big.LITTLE processing with
heterogeneous core blocks in 2021, as will be briefly discussed in the next Section.
Remark to Intel’s symmetrical multicore processors
Intel’s x86-based client or server processors are traditionally built up as symmetrical
multicores, up to the 11th gen. Tiger Lake family,
as depicted below for the 10-core 10th gen. Comet Lake client processor.

## Slide 106: 3.3.3 Armv7-based 32-bit symmetrical multicore CPUs (10)
Symmetrical
multicores
big-little
core clusters
Single-core
processors
Armv7-based CPU designs in mobile processors
Use of Armv7-based 32-bit symmetrical multicore CPUs in mobile processors
Cortex-A5/A9
HP: Cortex-A15/A17
LP: Cortex-A7
Armv7-A
CPUs
Cortex-A8
A5 (2011)
(2C)
Apple
4412 4C (2012)
7 7580 2x4C (2015)
5410 (4+4)C (2013)
5420 (4+4)C (2013)
Samsung
Exynos
8260 2C (2013)
400 4C (2013)
Qualcomm
Snapdragon
Huawei
Kirin
920 (4+4)) 2014)
(K3V2 4C (2012)
620 2x4C (2014)
MediaTek
MT6582 4C (2013)
MT6592 2x4C (2013)
MT8135 (2+2)C (2013)
MT6595 (4+4)C (2014)
APL2298 1C (2009)
QSD8250 1C (2007)
(A8-based Scorpion core)
3110 1C (2010)
CC interconnect
CC interconnect
MT6515 1C (2012)
MT6575 1C (2012)

## Slide 107: 3.3.3 Armv7-based 32-bit symmetrical multicore CPUs (11)
Example: Block diagram of a 32-bit quad-core symmetrical multicore
(Qualcomm’s Snapdragon 800 SOC) (2013) [40]
Note that there are two interconnects; the “Fabric” is cache coherent, while the
“Multimedia Fabric” is not.

## Slide 108
3.3.4 Armv7-based 32-bit big.little CPUs
This Subsection is part of the Lecture and the exam.
Notes: 108

## Slide 109: 3.3.4 Armv7-based 32-bit big.little CPUs (1)
Symmetrical multicore
CPUs
big-little
CPUs
Single-core
CPUs
Armv7-based 32-bit CPU designs in mobile processors
3.3.4 Armv7-based 32-bit big.little CPUs
CC interconnect
CC interconnect
(~2011-2013)
(~2013-2016)
(≈2007-2012)
Cortex-A5/A9
Cortex-A7/A15/A17
Cortex-A8
Typical Armv7 CPUs

## Slide 110: 3.3.4 Armv7-based 32-bit big.little CPUs (2)
big.little core clusters-based mobile processors -2
When ARM announced big.little processing in 2011, it triggered a transition from
the symmetrical multicore to big.little processor architectures, as demonstrated
in the following Figure.

## Slide 111: 3.3.4 Armv7-based 32-bit big.little CPUs (3)
Symmetrical
multicore CPUs
big.little
CPUs (core clusters)
Single-core
CPUs
Overview of Armv7 A-based CPU designs and their use in mobile processors
Use of Armv7-A based 32-bit big.little CPU design in mobile processors -1
Cortex-A5/A9
HP: Cortex-A15/A17
LP: Cortex-A7
ARM CPUs
Cortex-A8/A9
A5 (2011)
(2C)
Apple
4412 4C (2012)
5410 (4+4)C (2013)
5420 (4+4)C (2013)
Samsung
Exynos
8260 2C (2013)
400 4C (2013)
Qualcomm
Snapdragon
Huawei
Kirin
920 (4+4)) 2014)
(K3V2 4C (2012)
MediaTek
MT6582 4C (2013)
MT6592 2x4C (2013)
MT8135 (2+2)C (2013)
MT6595 (4+4)C (2014)
APL 2298 1C (2009)
QSD8250 1C (2007)
(A8-based Scorpion core)
3110 1C (2010)
CC interconnect
CC interconnect
MT6515 1C (2012)
MT6575 1C (2012)

## Slide 112: 3.3.4 Armv7-based 32-bit big.little CPUs (4)
The previous Figure illustrates that 32-bit big.little CPUs were introduced in Armv7-based
processors primarily around 2013-2014.
Use of Armv7-A based 32-bit big.little CPU design in mobile processors -2

## Slide 113: 3.3.4 Armv7-based 32-bit big.little CPUs (5)
Remarks: Introducing the big.little technology in x86-based processors
In 2020, Intel entered the client processor market with two Lakefield processor
models.
These processors were big. little CPU design with one big and 4 little cores.
They had a TDP of 7 W, used 3D packaging, and were aimed at 2-in-1
or lightweight laptops.
The Lakefield line was a pivotal design without a generation identifier.
Following this, in 2021, Intel unveiled an improved big.little processor family
called the 12th gen. Alder Lake family, manufactured using Intel 7 technology.
Alder Lake processors can have up to 8 big and up to 8 little cores.
The processor family covers all processor segments, from mobiles to servers.
Next, in 2022, Intel launched its 13th gen. Raptor Lake family, which has up to 8
big cores and up to 16 little cores manufactured using further on using the
Intel 7 technology.
At last, also AMD has introduced big.little architectures, with their Zen 4/Zen4c-based
Ryzen laptop APU (7440U) processors in 2023.

## Slide 114: 3.3.4 Armv7-based 32-bit big.little CPUs (6)
The rationale for big.little processing [41]
When
high-intensity loads will run on powerful but power-hungry cores, whereas
low-intensity loads on less powerful but less power-hungry cores
the total power consumption will be reduced.
The primary goal of the big.little technology is to reduce power consumption.
This concept is rooted in the recognition that the workload of smartphone or tablet processors fluctuates dynamically, i.e., high-intensity and low-intensity processor demands alternate, as shown in a subsequent Figure.

## Slide 115: 3.3.4 Armv7-based 32-bit big.little CPUs (7)
Example: Percentage of time spent in different processor states for less demanding
workloads in a dual-core mobile device [42] -1
The graph above displays the percentage of time spent in active states, idle states,
and shutdown states in a dual-core Cortex-A9-based mobile device.
In the diagram, red indicates the highest, green the lowest frequency operating
points, whereas colors in between represent intermediate frequencies.
Light blue means that the core is idling since Waiting for Interrupt (WFI), while
dark blue indicates that the core or both cores are shut down.
(Core)
WFI: Waiting for Interrupt
Wait for interrupt

## Slide 116: 3.3.4 Armv7-based 32-bit big.little CPUs (8)
In the diagram, both cores are mostly idle, shut down, or in the light-intensity
states.
This means that there is plenty of headroom for power saving when using
less powerful but less power-hungry cores during light intensity, idle, or
shut down phases of the operation.
Example: Percentage of time spent in DVFS states for low intensity
use cases in a mobile device [42] -2

## Slide 117: 3.3.4 Armv7-based 32-bit big.little CPUs (9)
Task forwarding
to a dedicated accelerator
Task migration
to different kind of CPUs
Task distribution policies in heterogeneous multicore processors
Master/slave
processing
Heterogeneous
attached processing
Heterogeneous
master/slave processing
Heterogeneous
big.LITLE processing
There is a master core (MCP)
and several slave cores.
The master core coordinates
the operation of the slave cores
to execute a task.
Beyond the CPU there are
dedicated accelerators,
such as a GPU, available.
An instruction will be
issued to an accelerator
when it will execute
the instruction more efficiently
than the CPU.
There are two or more core clusters with
different power/performance characteristics,
e.g., two clusters, a little and a big one.
The cores of the little cluster execute
less demanding tasks and consume
less power, while the cores of the big
cluster execute more demanding tasks
with higher power consumption.
MPC
CPU
GPU
Slave cores
Remark: The big.little technology is an alternative task distribution policy
in heterogeneous multicore processors
E.g., the Cell processor from
IBM/Sony/Toshiba (2006).
Widely used in mobiles.
Widely used in mobiles.

## Slide 118: 3.3.4 Armv7-based 32-bit big.little CPUs (10)
Principle of implementing big.little processing -1 [43]

## Slide 119: 3.3.4 Armv7-based 32-bit big.little CPUs (11)
Let’s interconnect these clusters by a cache-coherent interconnect to have
a multicore processor, as shown in the Figure above.
CPU0
CPU1
CPU2
CPU3
Cache coherent interconnect
Cluster of
little cores
Cluster of
big cores
CPU0
CPU1
CPU2
CPU3
To memory
Figure: A big.little configuration
consisting of two core clusters
Principle of implementing big.little processing -2
Let’s have two or more clusters of architecturally identical cores in a CPU.
a cluster of low-performance/low-power cores, termed the little cores and
a cluster of higher performance, higher power cores, termed the big cores,
as seen in the Figure below.
For example, let’s consider two clusters, each including four cores;

## Slide 120: 3.3.4 Armv7-based 32-bit big.little CPUs (12)
Principle of implementing big.little processing -3 [44]
at any time, either the big or the little core cluster is operatonal and
all cores of the big or little cluster operate at the same operating point
i.e., at the same clock frequency and core voltage,given
as indicated in the next Figure.
There are several alternatives to implement big.little technology, as discussed
in another Chapter of this Lecture Notes.
However, to provide a conceivable description of its principle of operation, let’s assume a specific implementation known as “exclusive cluster switching” when

## Slide 121: 3.3.4 Armv7-based 32-bit big.little CPUs (13)
Example: The operating points of a multicore processor which consists up
of two core clusters:
one with little cores (Cortex-A7) and one with big cores (Cortex-A15), as
described above [45]

## Slide 122: 3.3.4 Armv7-based 32-bit big.little CPUs (14)
Examples of big (Cortex-A15) and little cores (Cortex-A7) [45]

## Slide 123: 3.3.4 Armv7-based 32-bit big.little CPUs (15)
Performance and energy efficiency comparison of Cortex-A15 vs. Cortex-A7
cores while running different workloads [45]

## Slide 124: 3.3.4 Armv7-based 32-bit big.little CPUs (16)
Principle of operation [44]
Let’s suppose that the device is running under an appropriate OS routine,
such as the cpufreq kernel routine of Linux, which tracks the workload and
adjust the operating points accordingly.
As long as the OS routine estimates that the actual workload can be handled
by the „little” core cluster, it activates only its cores.
If, however, the workload surpasses the performance capability of the “little” core
cluster, the high-performance cores of the “big” cluster are activated, and a
cluster switch will occur, i.e., the actual workload is migrated from the cores
of the “little” cluster to the cores of the “big” cluster.
The cores of the “little” cluster are then turned off.
Conversely, if the OS recognizes that the workload can be managed by the “little”
cluster alone, it initiates a cluster switch back to the “little” cluster in the same
manner as described above.
This way, at any given time, only cores of one cluster can be active, and the
choice of which cluster is activated depends on the intensity of the workload.
This type of big.little technology is referred to as Exclusive cluster switching.

## Slide 125: 3.3.4 Armv7-based 32-bit big.little CPUs (17)
Illustration of the described model of operation [46]
Note that the little (A7) cluster is operational at low load, while the big (A15) cluster
is operational at high load.

## Slide 126
3.4 Armv8.0-A ISA-based 64-bit Cortex-A CPUs
Notes: 126

## Slide 127: 3.4 Armv8.0-A ISA-based 64-bit Cortex-A CPUs (1)
3.4 Armv8.0-A ISA-based 64-bit Cortex-A CPUs
Section 3.3
Section 3.5
Section 3.6
Cortex-A8
Cortex-A57/A53
Cortex-A75/A55
Cortex-X2/A710/A510
First CPUs
Section 3.4
based on
the 32-bit Armv7-A ISA
Cortex-A CPUs
based on
the Armv8.0-A ISA
based on
the Armv8.2-A ISA
based on
the Armv9-A ISA

## Slide 128: 3.4 Armv8.0-A ISA-based 64-bit Cortex-A CPUs (2)
Overview of Armv8.0-A ISA-based 64-bit Cortex-A CPUs (based on [36])
2012
2013
10/2009
Cortex-A5
Armv7
40 nm
High Performance
Mainstream
Low power
Announced
1
2
3
4
5
2006
2007
2008
2009
2010
2011
10/2011
Cortex-A7
Armv7
28 nm
10/2012
Cortex-A53
Armv8
20/16 nm
10/2005
Cortex-A8
Armv7
65 nm
10/2007
Cortex-A9
Armv7
40 nm
9/2010
Cortex-A15
Armv7
32/28 nm
10/2012
Cortex-A57
Armv8
20/16 nm
2014
2/2014
Cortex-A17
Armv7
28 nm
6
7
DMIPS/MHz
2015
2/2015
Cortex-A72
Armv8
16 nm
11/2015
Cortex-A35
Armv8
16/14 nm
8
2016
5/2016
Cortex-A73
Armv8
10 nm
6/2013
Cortex-A12
Armv7
28 nm
Armv7-A
(32-bit)
Armv8.0-A
(64-bit)
(Dhrystone MIPS: relative performance vs. the
DEC VAX 11/780 minicomputer).
(Dhrystone: a synthetic benchmark for syst. progr.).

## Slide 129: 3.4 Armv8.0-A ISA-based 64-bit Cortex-A CPUs (3)
CPU Core | Announced | Available in devices | Target category | L2 cache | Multicore support (MPCore) | big.little support | Efficiency DMIPS/MHZ
Cortex-A53 | 2012 | H2/2014 | Low power | Mandatory | Yes | Yes | 2,3
Cortex-A57 | 2012 | H2/2014 | High-end |  |  |  | 4,8
Cortex-A72 | 2015 | 2016 | High-end |  |  |  | 6.3-7.3
Cortex-A73 | 2016 | 2017 | High-end |  |  |  | 7.4-8.5
Main features of Armv8.0-A ISA-based 64-bit Cortex-A CPUs [47]
As indicated, Armv8.0-based cores are 64-bit designs, have mandatory, shared L2 caches,
and support big.little processing.

## Slide 130: 3.4 Armv8.0-A ISA-based 64-bit Cortex-A CPUs (4)
Use of 64-bit Armv8.0-based CPUs in mobile processors -1
Armv8.0-based processors were first used in symmetrical multicore and then
in big.little designs, as shown in the following Figure.
Remark
Symmetrical multicore and big.little CPU designs were previously discussed in Sections
3.3.3 and 3.3.4, so for related details we refer to the mentioned sections.

## Slide 131: 3.4 Armv8.0-A ISA-based 64-bit Cortex-A CPUs (5)
64-bit Armv8.0-Arm9.0-based CPU designs in mobile processors
DynamIQ
core clusters
Symmetrical
multicores
Armv9-A based
DynamIQ core clusters
ARM cores
Cortex-A53
HP: Cortex-A57/
A72/A73
LP: A53
HP: Cortex-A75/A76/
A77/A78/X1
LP: A55
HP: Cortex-X2
MS: A-710
LP: A-510
ARM ISA
Armv8.0
Armv8.0
Armv8.2
Armv9.0
Apple
Samsung
Exynos
Qualcomm
Snapdragon
Huawei
Kirin
MediaTek
9810 (2018)
(4+4)C
845 (2018)
(4+4)C
980 (2018)
(2+2+4)C
Helio P90 (2+6)C (2019)
2200 (2022)
(1+3+4)C
8 Gen 1(2022)
(1+3+4)C
A11 (2017)
(2+4)C
Processors
A10 (2016)
(2+2)C (Armv8.1)
620 (2014)
2x4C
7 7580 (2015)
8C
8 8890 (2016)
(4+4)C
439 (2018)
(4 +4)C
650 (2016)
(4+4)C
MT6735 (2015)
4C
MT6750 (2016)
(4+4)C
A7 (2013)
2C
410 (2014)
4C
Dimensity 9000 (1+3+4)C (2021)
big.little
core clusters
CC interconnect
CC interconnect
CC interconnect
CC interconnect
Use of 64-bit Armv8.0-based CPUs in mobile processors -2

## Slide 132: 3.4 Armv8.0-A ISA-based 64-bit Cortex-A CPUs (6)
Use of 64-bit Armv8.0-based CPUs in mobile processors -3
As the previous Figure shows, Armv8.0-based processors initially emerged as
symmetrical multicores around 2013 and 2016, rather than as big.little designs.
They were mostly built using the Cortex-A53 and A57 cores.
Over time, these processors began to be used more frequently in big.little
core clusters between 2016 and 2018, as depicted in the Figure.

## Slide 133
3.5 Armv8.2-A ISA-based 64-bit Cortex-A CPUs
a
Notes: 133

## Slide 134: 3.5 Armv8.2-A ISA-based 64-bit Cortex-A CPUs (1)
64-bit Armv8.0-Arm9.0-based CPU designs in mobile processors
DynamIQ
core clusters
Symmetrical
multicores
Armv9-A based
DynamIQ core clusters
ARM cores
Cortex-A53
HP: Cortex-A57/
A72/A73
LP: A53
HP: Cortex-A75/A76/
A77/A78/X1
LP: A55
HP: Cortex-X2
MS: A-710
LP: A-510
ARM ISA
Armv8.0
Armv8.0
Armv8.2
Armv9.0
big.little
core clusters
CC interconnect
CC interconnect
CC interconnect
CC interconnect
3.5 Armv8.2-A ISA-based 64-bit Cortex-A CPUs
In 2017, the Armv8.2 ISA revision was issued and 64-bit big.little core clusters
gave way to DynamIQ core clusters.
This move aimed to provide greater design flexibility and improve power efficiency.
DynamiQ core clusters can include up to 8 cores from two core types (as seen below),
and include a monolithic (not sliced) L3 cache.
Figure: Emergence of CPU designs built up on Armv8.2-based DynamIQ core clusters

## Slide 135: 3.5 Armv8.2-A ISA-based 64-bit Cortex-A CPUs (2)
Let’s become acquainted with DynamIQ core clusters -1
ARM began developing the DynamIQ core cluster technology in 2013 [48].
It was released in 04/2017 along with the Armv8.2-A ISA.
The DynamIQ core cluster technology is an enhancement upon the big.little
core clusters design, as shown in the following Figures.

## Slide 136: 3.5 Armv8.2-A ISA-based 64-bit Cortex-A CPUs (3)
Let’s become acquainted with DynamIQ core clusters -2
It represents the third step in the evolution of the core cluster technology.
Figure: Evolution steps of the core cluster technology [49]
ARM11 MPCore (2004)
Cortex-A7/A15 (~2011)
Cortex-A55/A75 (~2017)
SMP
(
)

## Slide 137: 3.5 Armv8.2-A ISA-based 64-bit Cortex-A CPUs (4)
To
DynamIQ core clusters contrasted with big.little core clusters – an overview
A single DynamIQ core cluster [50]
Key features
Based on Armv7/v8-A (2011)
Dual clusters, up to 4 cores each
Based on Armv8.2-A (2017)
Single cluster, up to 8 cores (up to 4b), two core types
with different core mixes
To a cache coherent interconnect through the AMBA4 ACE bus
CPU0
CPU1
CPU2
CPU3
Cache coherent interconnect
Cluster of
little cores
Cluster of
big cores
CPU0
CPU1
CPU2
CPU3
big and little core clusters
(2011)
L2 cache
L2 cache

## Slide 138: 3.5 Armv8.2-A ISA-based 64-bit Cortex-A CPUs (5)
What are the key enhancements of the DynamIQ core clusters?
DynamIQ core clusters introduced three key enhancements to ARM architectures.
These enhancements will be detailed in the following.

## Slide 139: 3.5 Armv8.2-A ISA-based 64-bit Cortex-A CPUs (6)
Armv8.2-A support,
2 core types, up to 8 cores but only up to 4b/cluster,
E.g. Cortex-A75/55 and subsequent Cortex-A7x cores
Up to 8 Armv8.2-A cores of two core types instead of up to 4 Armv7/v8.0 cores
of the same core type
Armv7/v8.0-A support,
single core type, up to 4 cores/cluster
E.g. Cortex-A53/A57/A72/A73,
big or little core cluster (2015) [51]
DynamIQ core cluster (2017) [50]
Cortex-A73 core
Armv8.0 CPU

## Slide 140: 3.5 Armv8.2-A ISA-based 64-bit Cortex-A CPUs (7)
DynamIQ core clusters may include two types of Armv8.2-A compatible cores, such as
Use of Armv8.2-A cores in DynamIQ core clusters
the high-performance Cortex-A75/A76/A77/A78/X1 and
the low-performance/high-efficiency Cortex-A55
cores.
Note that starting with Armv8.2-A-based cores, ARM no longer organizes its cores
in typically two 4-core core blocks, instead it make use of DynamIQ core clusters
with up to 8 big or little cores.

## Slide 141: 3.5 Armv8.2-A ISA-based 64-bit Cortex-A CPUs (8)
b) Private (per-core) L2 caches instead of a shared L2 cache
Cortex-A73 core
Armv8.0 CPU
big or little core cluster (2015) [51]
DynamIQ core cluster (2017) [50]
Armv8.0-A support, e.g. Cortex-A53/
A57/A72/A73, up to 4 cores/cluster
Shared L2 cache
Armv8.2-A support, (Cortex-A55/75)
2 CPU types, up to 8 cores but only 4b/cluster
Private L2 caches

## Slide 142: 3.5 Armv8.2-A ISA-based 64-bit Cortex-A CPUs (9)
c) DynamIQ Shared Unit (DSU) with a shared (not sliced) L3 cache and snoop filter [52]
(Up to two 128-bit AMBA 5 ACE,
or up to two 256-bit AMBA 5 CHI bus)
(Per-core DVFS control,
Partial L3 power down)
(Partitions)
(Snoop filter)
(L3 cache)
Remark [89]
The snoop filter records the addresses of data that are kept in the caches in various cores.
By keeping track of which caches hold copies of specific data blocks a snoop filter
can prevent unnecessary snoop requests to caches that do not have the data
(shared, not sliced)

## Slide 143: 3.5 Armv8.2-A ISA-based 64-bit Cortex-A CPUs (10)
Reduced cache latencies in DynamIQ core clusters-based systems (in cycles) [52]
Armv8.2
Armv8.2
Armv8.0
Armv8.2

## Slide 144: 3.5 Armv8.2-A ISA-based 64-bit Cortex-A CPUs (11)
Main benefits of DynamIQ core clusters
greater flexibility due to up to two core types and up to 8 cores with different mixes
redesigned cache subsystem with lower access times
improved power efficiency through intelligent power management (EAS)
(Energy Aware Scheduling). It’s not detailed here.
Up to 8 Armv8.2-A cores of two core types vs. up to 4 Armv7/v8.0-A cores of the
same core type
Private (per-core) L2 caches instead of a shared L2 cache
c) DynamIQ Shared Unit (DSU) with a shared (not sliced) L3 cache and snoop filter
Summary of the enhancements and main benefits of DynamIQ core clusters
Summary of the enhancements introduced in DynamIQ core clusters

## Slide 145: 3.5 Armv8.2-A ISA-based 64-bit Cortex-A CPUs (12)
Introduction of Armv8.2-A based Cortex-A cores [53]
Source: ARM
A7x
Series
A5x
Series
A3x
Series
Armv8.2-A
Armv8.0-A

## Slide 146: 3.5 Armv8.2-A ISA-based 64-bit Cortex-A CPUs (13)
Cortex model | ISA | Launched in | Target IC techn. | Decode width | Dispatch rate | Issue rate | ROB size
A55 | Armv8.2 | 05/2017 | 10 nm | 2 | 2 | 2 | -- (In-order design)
A75 | Armv8.2 | 05/2017 | 10 nm | 3 | 6 | 8 | 128
A76 | Armv8.2 | 05/2018 | 12, 7, 5 nm | 4 | 8 | 9 | 128
A77 | Armv8.2 | 05/2019 | 7, 5 nm | 4 | 6 | 12 | 160
A78 | Armv8.2 | 05/2020 | 5 nm | 4 | 6 | 13 | 160
X1 | Armv8.2 | 05/2020 | 5 nm | 5 | 8 | 15 | 224
Main features and evolution of Armv8.2-based Cortex-A cores
Note that Arm has dynamically increased the decode width of its ARM8.2-based
big cores from 3 to 5.
Simultaneously, the vendor has raised both the dispatch and issue rates as well as
the ROB size to significantly enhance performance.

## Slide 147: 3.5 Armv8.2-A ISA-based 64-bit Cortex-A CPUs (14)
Use of 64-bit Armv8.2-based Cortex-A cores in mobile processors
DynamIQ
core clusters
Symmetrical
multicores
Armv9-A based
DynamIQ core clusters
ARM cores
Cortex-A53
HP: Cortex-A57/
A72/A73
LP: A53
HP: Cortex-A75/A76/
A77/A78/X1
LP: A55
HP: Cortex-X2
MS: A-710
LP: A-510
ARM ISA
Armv8.0
Armv8.0
Armv8.2
Armv9.0
Apple
Samsung
Exynos
Qualcomm
Snapdragon
Huawei
Kirin
MediaTek
9810 (2018)
(4+4)C
845 (2018)
(4+4)C
980 (2018)
(2+2+4)C
Helio P90 (2+6)C (2019)
2200 (2022)
(1+3+4)C
8 Gen 1(2022)
(1+3+4)C
A11 (2017)
(2+4)C
Processors
A10 (2016)
(2+2)C (Armv8.1)
620 (2014)
2x4C
7 7580 (2015)
8C
8 8890 (2016)
(4+4)C
439 (2018)
(4 +4)C
650 (2016)
(4+4)C
MT6735 (2015)
4C
MT6750 (2016)
(4+4)C
A7 (2013)
2C
410 (2014)
4C
Dimensity 9000 (1+3+4)C (2021)
big.little
core clusters
CC interconnect
CC interconnect
CC interconnect
CC interconnect
ARMv8.2-based DynamIQ core clusters were mostly used in mobiles between 2017-2019.

## Slide 148: 3.5 Armv8.2-A ISA-based 64-bit Cortex-A CPUs (15)
Example of an Armv8.2-A based premium mobile system (2018) [54]
CCI-550: Cache Coherent Interconnect CoreSight: Test/debug unit
MMU-500: Memory Management Unit (responsible for virtualization and caching)
NIC-450: Network Interconnect (interface converter)
GIC-600: General Interrupt Controller
SCP: System Control Processor

## Slide 149
3.6 Armv9-A based 64-bit Cortex-A CPUs

## Slide 150: 3.6 Armv9-A based 64-bit Cortex-A CPUs (1)
3.6 Armv9-A based 64-bit Cortex-A CPUs -1
64-bit Armv8.0-Arm9.0-based CPU designs in mobile processors
DynamIQ
core clusters
Symmetrical
multicores
Armv9-A based
DynamIQ core clusters
ARM cores
Cortex-A53
HP: Cortex-A57/
A72/A73
LP: A53
HP: Cortex-A75/A76/
A77/A78/X1
LP: A55
HP: Cortex-X2
MP: A-710
LP: A-510
ARM ISA
Armv8.0
Armv8.0
Armv8.2
Armv9.0
big.little
core clusters
CC interconnect
CC interconnect
CC interconnect
CC interconnect
HP: High-Performance
MP: Middle-Performance
HE: High-Efficiency

## Slide 151: 3.6 Armv9-A based 64-bit Cortex-A CPUs (2)
Armv9-A based 64-bit Cortex-A CPUs -2
Figure: Evolution of the Arm ISA after the Armv3 release
4.5 Armv9-A based DynamIQ core clusters-based mobile processors (1)
In 03/2021 ARM announced the Armv9-A ISA, later renamed as Armv9.0 ISA.
This revision enhanced vector processing, ML, and security (as indicated below).
It also introduced Armv9-A-based DynamIQ core clusters (as detailed in this Section).
Adv. SIMD (NEON)
(SVE2)

## Slide 152: 3.6 Armv9-A based 64-bit Cortex-A CPUs (3)
Armv9.2-A ISA and CPUs based on the Armv9.2-A
In 05/2023, ARM released the Armv9.2 ISA update with several minor enhancements
of the Armv9.0 version (not discussed here).
In the following, we will describe Armv9.0-A and Armv9.2-A-based CPUs together
as Armv9-A-based CPUs.

## Slide 153: 3.6 Armv9-A based 64-bit Cortex-A CPUs (4)
Armv9-A-based DynamiQ core clusters represent the next step in the evolution of
CPU configurations.
Unlike the previous Armv8.2 core clusters, the new core clusters may include
three core types out of 8 cores, rather than only two, as in the previous Armv8.2
DynamIQ core clusters, and offer additional improvements as well, as discussed
subsequently.
Armv9-A based DynamIQ core clusters -1

## Slide 154: 3.6 Armv9-A based 64-bit Cortex-A CPUs (7)
What are the key enhancements of the Armv9-A based DynamIQ core clusters?
Use of up to three core types rather than only two, as before.
Sliced L3 caches, snoop filter, and the control logic.
The memory Tagging Extension (MTE).
Wider (scalable) bus interfaces.
Subsequently, we will discuss the enhancements mentioned above.

## Slide 155: 3.6 Armv9-A based 64-bit Cortex-A CPUs (8)
a) Possible use of three core types rather than two as in DynamIQ core clusters [55]
The new DynamIQ core cluster may have up to 8 cores out of 3 core types:
high-performance Cortex-X2 (X) cores (even 8 Cortex-X cores),
middle-performance Cortex-A710 (L) cores and
high-efficiency Cortex-A510 (b) little cores,
while the specific mix of the cores depends on the type of device being targeted.
Figure: Use cases of Armv9-based CPU cores [55]

## Slide 156: 3.6 Armv9-A based 64-bit Cortex-A CPUs (9)
b) Sliced L3 cache, snoop filter and the control logic [55]
In the new DynamIQ core cluster the L3 cache, snoop filter, and control logic are
sliced, as indicated in the Figure below.
Figure: Sliced implementation
of the L3 cache, snoop filter
and the control logic

## Slide 157: 3.6 Armv9-A based 64-bit Cortex-A CPUs (10)
The cores are connected to
the L3 slices.
A ring-based transport network
interconnects the L3 slices
and the bus interface.
There are dual bi-directional
rings present.
Traffic can take either direction
to reduce delay.
Interconnection of the slices [55]

## Slide 158: 3.6 Armv9-A based 64-bit Cortex-A CPUs (11)
The cache is a single entity, accessible at a single point.
All accesses are equally long (uniform).
The cache consists of multiple interconnected slices (segments) that operate independently, enabling
parallel access.
However, cache accesses may be non-uniform,
varying in length.
C
C
C
C
L3 $
C
C
C
C
L3 slice 0
L3 slice 1
L3 slice 2
L3 slice 0
L3 caches
(They are mostly unified (for instructions and data) and shared by all cores).
They can be built up either as not sliced (homogeneous) or sliced.
Not sliced
Sliced
Principle of sliced L3 caches

## Slide 159: 3.6 Armv9-A based 64-bit Cortex-A CPUs (12)
Figure: Parallel operating cache slices increase the L3 memory bandwidth [55]
Slices of sliced L3 caches can operate in parallel.
So sliced caches with n slices have, in principle, an n-times higher memory
bandwidth than unsliced caches, as indicated in the Figure below.
Major benefits of sliced L3 caches -1

## Slide 160: 3.6 Armv9-A based 64-bit Cortex-A CPUs (13)
Major benefits of the sliced L3 caches -2
2) Smaller cache slices have lower access times than a large cache.

## Slide 161: 3.6 Armv9-A based 64-bit Cortex-A CPUs (14)
if the requested data is held in the accessed slice, it can be accessed with
a lower access time,
b) alternatively, if the requested data is stored in a remote slice, the access time
will be longer.
It follows that cache access times are now non-uniform; a sliced cache behaves
as a NUCA (Non-Uniform Cache Architecture).
When accessing sliced caches there are two access patterns:
Consequence of slicing the L3 cache – non-uniform cache accesses

## Slide 162: 3.6 Armv9-A based 64-bit Cortex-A CPUs (15)
Additional enhancements while increasing the new DynamIQ core cluster
In addition, the size of the L3 cache has been raised from up to 4 MBs (in the
previous generation) to up to 16 MB to improve performance and lower power
consumption.
Also, the operation frequency of the L3 cache has been increased to enhance
bandwidth and reduce latencies.

## Slide 163: 3.6 Armv9-A based 64-bit Cortex-A CPUs (16)
3-level cache architectures
Per-core, unified L2 cache
Shared, unified L3 cache
Not sliced
Sliced
Core 2 based
Nehalem 4C
(2008)
Core 2 based
Sandy Bridge 4C
(2011)
and subsequent proc.
K10 Barcelona
(2007)
Intel
AMD
K17 Zen core-based lines
(2017)
v8.2-A based cores
(2016)
ARM
v9-A based cores
(2021)
It is worth noting that L3 caches of Intel’s or AMD’s client and ARM’s mobile Cortex
cores followed the same evolution paths,
namely, initially, all mentioned companies used not sliced (homogeneous) L3 caches, but
later transitioned to sliced ones (as indicated below), primarily for higher performance
(cache bandwidth) achieved through parallel operating slices, as shown below.
Remarks to the emergence of sliced L3 caches

## Slide 164: 3.6 Armv9-A based 64-bit Cortex-A CPUs (17)
The importance of security issues concerning memory accesses
The Memory Tagging Extension addresses memory vulnerabilities.
According to Microsoft and Google, over 70-75 % of vulnerabilities stem from
memory safety issues (like buffer overflow-based threats) [56]
c) The Memory Tagging Extension (MTE)
Although it was introduced already in the Armv8.5 ISA version as an optional feature,
in 2018, it became mandatory only in the Armv9.0 release.

## Slide 165: 3.6 Armv9-A based 64-bit Cortex-A CPUs (18)
Memory tagging is implemented using locks and keys.
Locks are set in the memory and keys are associated with virtual memory addresses.
Access is permitted if the key matches the lock, if not, an error occurs and
an exception is generated.
Figure: Using memory locks and
access keys to protect memory
against safety violations.
Principle of memory tagging [48]

## Slide 166: 3.6 Armv9-A based 64-bit Cortex-A CPUs (19)
Principle of implementing memory tagging in Armv9 MTE extension -1 [57]
Top byte of the adress
(CI: Coherent Interconnect)
MTE provides locks to memory locations by adding a four-bit tag to each 16 bytes
of the physical memory.
The tags are implemented in the System Level Cache (SLC) of the CI-700 (not discussed).

## Slide 167: 3.6 Armv9-A based 64-bit Cortex-A CPUs (20)
4-bit keys, on the other hand, are attached to the virtual addresses, as depicted
below.
This solution has become feasible, as Armv8-A architectures do not use the
top byte of virtual addresses.
Top byte of the adress
Principle of implementing memory tagging in Armv9 MTE extension -2 [57]

## Slide 168: 3.6 Armv9-A based 64-bit Cortex-A CPUs (21)
d) Wider (scalable) bus interface [55]
The Scalable bus interface to the Cache Coherent Interconnect (CI-700) has been
significantly enhanced by providing up to 4 256-bit wide bus interfaces, while
utilizing an updated AMBA CHI bus protocol to achieve higher bandwidth and
MTE support.
By comparison, the previous
Armv8.2-A based DynamIQ core
cluster provided a 2x256-bit or
2x128-bit wide bus interface
(implementation dependent).

## Slide 169: 3.6 Armv9-A based 64-bit Cortex-A CPUs (22)
Armv9-based Cortex-A CPUs
Armv9-based Cortex-A CPUs include the Armv9.0-A and Arm9.2-A based cores.
They belong to three core types, called the
big
middle and
little
cores.
The above core types are implemented in three core series, as follows:
Cortex-X series cores
Cortex-A700 series cores and the
Cortex-A500 series cores,
as indicated and described in the following Figure.

## Slide 170: 3.6 Armv9-A based 64-bit Cortex-A CPUs (23)
Design goals of the Armv9-A ISA based Cortex-A core series [58]
The Cortex-X series are maximum performance big cores for single thread burst workloads.
The Cortex-A700 series are middle cores, balanced for efficiency and performance for
multi-core workloads.
The Cortex-A500 series are efficient little cores for background and lightweight workloads.

## Slide 171: 3.6 Armv9-A based 64-bit Cortex-A CPUs (24)
The Cortex-X and Cortex-A700 series cores are traditional single-core CPUs, while
the Cortex-500 series are dual-core core modules (called core complexes).
The core modules of the Cortex-500 series include dual FX cores and dual but shared
NEON/SVE2 SIMD units with a shared L2 cache, as will be discussed later.
Now, we are about to unveil the first introduced models of the Armv9-A-based core series,
which represent a significant milestone in mobile processors.
Layout of the Armv9-A ISA based Cortex-A core series [58]

## Slide 172: 3.6 Armv9-A based 64-bit Cortex-A CPUs (25)
Cortex-X2
512 KB/1 MB
Cortex-A710
First Armv9.0-based Cortex-X and Cortex-A700 series cores:
the Cortex-X2 and the Cortex-A710 cores (2021) [58]

## Slide 173: 3.6 Armv9-A based 64-bit Cortex-A CPUs (26)
Remark to the Cortex-X series
The Cortex-X series was introduced in 2020 as a series of extremely high-performance
cores, along with the Cortex-X Custom Program, which will be described next.

## Slide 174
It enhances the former “Built on ARM Cortex Technology” licensing model.
Under the enhanced "Built on ARM Cortex Technology" licensing model, licensees
can customize standard ARM Cortex products for “performance-first” designs.
This customization may include e.g., increasing the size of the ReOrder Buffer (ROB),
which can improve performance but requires more power and a larger silicon area.
The customization process involves early collaboration between ARM and the
licensee, but ARM carries out the design.
In the new scheme, ARM retains the ARM Cortex branding for the cores, so
licensee-specific core names are not permitted.
The extra high-performance Cortex-X series CPUs are exclusively available to
Cortex-X Custom Program licensees.
The first member of the Cortex-X series is the Armv8.2-based Cortex-X core
(introduced in 2020).
3.6 Armv9-A based 64-bit Cortex-A CPUs (27)
ARM’s Cortex-X Custom Program (2020) [59]

## Slide 175: 3.6 Armv9-A based 64-bit Cortex-A CPUs (28)
Cortex-A710
ARM’s Cortex-A510 core module (core complex) includes dual FX cores with per-core
front-ends and execution units.
It also features dual, shared 64-bit or 128-bit wide NEON/SVE2 SIMD execution units,
along with an up to 512 KB shared L2 cache, as indicated in the Figure above.
First Armv9.0-based Cortex-A500 series core module (core complex):
the Cortex-A510 (2021) [58]

## Slide 176: 3.6 Armv9-A based 64-bit Cortex-A CPUs (29)
Remark to ARM’s Cortex-500 series core modules
Figure: AMD’s module concept introduced in the
Buldozer line in 2011 [60]
ARM’s Cortex-500 core modules are similar to AMD’s Bulldozer modules from 2011.
There is, however, a notable difference in both concepts because the A510 has
separate front-ends while AMD’s modules do not.
AMD’s design style has the drawback of lproviding low FP and SIMD performance,
which became detrimental to the fate of the Bulldozer line of processors.
ARM justifies its module concept by pointing out that reducing FP- and SIMD performance
does not seem unfavorable for the little cores since FP and vector workloads are
expected to run on big CPU cores rather than on little cores.

## Slide 177: 3.6 Armv9-A based 64-bit Cortex-A CPUs (30)
How can three core types be utilized for efficient big.little processing?
Cortex-A715
Cortex-X3
Cortex-A510
While continuously selecting the optimal core for execution, processor consumption or
processor efficiency is optimized.
The power-performance curves of the cores reveal the answer.
Figure: Power-performance curves of 2. gen. Armv9.0-based cores [61]

## Slide 178: 3.6 Armv9-A based 64-bit Cortex-A CPUs (31)
Introducing the Total Compute Solutions (TCSs) concept along with the
Armv9.0-A ISA
TCSs are Armv9-based, optimized platforms, announced in 05/2021.
They have four essential components:
ARM updates their TCSs annually and uses a suffix in the designation to indicate
the year of introduction, such as TCS21, TCS22, etc.
Since we are focusing on Armv9-A-based DynamIQ core clusters, we will only
be concerned with Armv9-A-based cores and DynamIQ Shared Units (DSUs) while
excluding Mali GPUs and the CoreLink data interconnects.
In the Figure below, we display the core- and DSU components of the initially
introduced TCS21 platform and compare their performance and efficiency with
previous implementations.
Armv9-based Cortex cores,
the DSU (DynamIQ Shared Unit)
a Mali GPU and
dual CoreLink data interconnects.

## Slide 179: 3.6 Armv9-A based 64-bit Cortex-A CPUs (32)
3.4.1 Main extensions of the Armv9.0 ISA
Introduction of the Armv9.0-based Total Compute Solutions (TCS) platform
concept in 2021 [58]
Note that the TCS21 platform comprises not only the cores but also the DSU 110
(DynamIQ Shared Unit), interconnect networks (CoreLink), and the GPU (Mali 710).

## Slide 180: 3.6 Armv9-A based 64-bit Cortex-A CPUs (33)
DynamIQ core clusters are essential parts of Armv9-based Total Compute Solutions.
They are composed of Armv9-based cores and the DSU (DynamIQ Shared Unit).
The max. core count varies depending on the TCS platform generation, as discussed later.
When considering the max. core count, Cortex-A500 modules count as 2.
For example, the Figure below shows the key components of the first-generation
Armv9-based DynamIQ core clusters, which can include up to 8 Cortex-X2/A710/A510
cores and the DSU-110 DynamIQ Shared Unit.
Figure: Armv9.0 based DynamIQ core cluster with up to 8 Cortex-X2/A710/A510 cores
and the DSU-110 DynamIQ Shared Unit
The role of DynamIQ Core clusters in ARM’s Total Compute Solutions concept 58]
We note that the DSU-110 also includes a shared, up to 16 MB-sized L3 cache.

## Slide 181: 3.6 Armv9-A based 64-bit Cortex-A CPUs (34)
Armv9-based mobile SoC with dual interconnects (2021) [62] -1
CoreLink CI-700: Cache-coherent mesh interconnect with system cache (L3 slices) and snoop filter.
CoreLink NI-700: Non-cache-coherent, packetized Network-on-Chip (NoC) interconnect to attach
accelerators and IO.
Ethos (NPU)
Mali (GPU)
DynamIQ
core cluster
CI-700 interconnects
DSI segments, cores,
MC, NI-700

## Slide 182: 3.6 Armv9-A based 64-bit Cortex-A CPUs (35)
Use of dual interconnects in Armv9-based mobile SoC (2021) [62] -2
The mobile SoC, shown in the previous Figure is built upon two interconnects; on
the Cache-coherent Interconnect CI-700 and
the Non-cache coherent interconnect NI-700.

## Slide 183: 3.6 Armv9-A based 64-bit Cortex-A CPUs (36)
Why have dual interconnects become prevalent in processors?
When a processor (or computer system) includes functional units with caches,
like CPU cores or accelerators and these functional units share the same
memory space, memory operations (reads and writes) have to maintain cache
coherency to always access the most recent copy of the referenced data.
This is achieved through using cache-coherent interconnects.
On the other hand, other functional units, like displays or IO controllers, do not
include caches and, therefore, do not require memory synchronization.
It follows that functional units without caches can be connected to the processor
or the system through a non-cache-coherent, less complex interconnect.
Therefore, system design can be optimized by using two interconnects - one
cache-coherent and another non-cache-coherent – to link system components.
The following two Figures provide examples of this design approach.
Use of dual interconnects in processors

## Slide 184
Example 1: Use of dual interconnects in processors:
Intel’s Atom processor-based SoC architecture, revealed at IDF 2010 [75]
3.6 Armv9-A based 64-bit Cortex-A CPUs (37)
The “low-power memory interconnect fabric” is presumably a ring bus.
There is no information about how the non-cache coherent IO fabric is implemented.
Cache coherent
fabric
Non-cache coherent
fabric

## Slide 185: 3.6 Armv9-A based 64-bit Cortex-A CPUs (38)
Example 2: Use of dual interconnects in processors:
Intel’s 11th gen. Tiger Lake processor (2020) [76]
The “Coherent fabric” is likely a ring bus.
There is no information about how the non-cache coherent fabric has been
implemented.

## Slide 186: 3.6 Armv9-A based 64-bit Cortex-A CPUs (39)
Evolution of ARM’s TCS generations [78]
Next, we provide more details of how TCS generations evolved.

## Slide 187: 3.6 Armv9-A based 64-bit Cortex-A CPUs (40)
Intro | Arm ISA | Big core | Middle core | Little core | DSU
05/2020 | Armv8.2 | Cortex-X1 | -- | Cortex-A55 | DSU Up to 8 cores (Up to 4 big cores) Up to 4 MB L3
Cortex-X1-based platform (the preceding platform before TCS-21)
(Announced in connection with the Cortex Custom Program)
Supports both the AArch32/64 execution modes)
Intro | Arm ISA | Big core | Middle core | Little core | DSU
05/2021 | Armv9.0 | Cortex-X2 Single core | Cortex-A710 Single core | Cortex-A510 Dual-core module | DSU-110 Up to 8 cores (Up to 8x X2) Up to 8 MB L3
CTS21 (Total Compute Solutions 21 Platform)
(Only the Cortex-710 CPU supports both the AArch32/64 execution modes)
Comparing the key components of the preceding Armv8.2-based Cortex-X1
platform with the subsequent Armv9.0-based TCS21 platform

## Slide 188: 3.6 Armv9-A based 64-bit Cortex-A CPUs (41)
Intro | Arm ISA | Big core | Middle core | Little core | DSU
05/2023 | Armv9.2 | Cortex-X4 Up to 2 MB L3 (instead of 1 MB) | Cortex-A720 | Cortex-A520 | DSU-120 Up to 14 cores (Up to 10xX4 + 4x A720 cores) Up to 32 MB L3
TCS23 (Total Compute Solutions 23 Platform) with the G720 Mali GPU
(Only Aarch64 support)
Evolution of ARM’s TCS generations
Intro | Arm ISA | Big core | Middle core | Little core | DSU
06/2022 | Armv9.0 | Cortex-X3 | Cortex-A715 | Updated Cortex-A510 | Updated DSU-110 Up to 12 cores (Up to 8 X3 + 4 A715 cores) Up to 16 MB L3
TCS22 (Total Compute Solutions 22 Platform) with the G715 Mali GPU
(Only the updated Cortex-A510 core module supports both Aarch32/64 modes)

## Slide 189: 3.6 Armv9-A based 64-bit Cortex-A CPUs (42)
Increasing core counts and L3 cache sizes in ARM’s TCS generations
As indicated in the previous Tables, ARM notably enhanced their DynamIQ core clusters
in two main aspects:
a) The max. number of supported cores was increased from 8 (TCS21) to 10 (TCS22)
and then to 14 (TCS23).
 | X1-based DSU | TCS21 DSU110 | TCS22 Updated DSU110 | TCS23 DSU120
L3 cache size (up to) | 4 MB | 8 MB | 16 MB | 32 MB
Table: Increasing maximum L3 cache sizes in the DSU Units
 | X1-based DSU | TCS21 DSU110 | TCS22 DSU110 | TCS23 DSU110
Max. number of supported cores | 8 | 8 | 12 | 14
Table: Max. number of cores supported by the DSU Units
b) The max. size of the L3 cache has been doubled in each new generation, as seen below:

## Slide 190: 3.6 Armv9-A based 64-bit Cortex-A CPUs (43)
The Cortex-X series cores are ARM’s flagship client cores, as pointed out previously,
so their evolution is an intriguing issue.
Therefore, firstly, we will summarize the key features of subsequent generations of
ARM Cortex-X cores, and then we will illustrate how ARM raised their performance
through widening the core width.
Evolution of the Cortex-X core series/

## Slide 191: 3.6 Armv9-A based 64-bit Cortex-A CPUs (44)
Arm Cortex-X Evolution | Cortex-X4 | Cortex-X3 | Cortex-X2 | Cortex-X1
Expected mobile clock speed | ~3.4 GHz | ~3.3GHz | ~3.0GHz | ~3.0GHz
Instruction decode width | 10? | 6 | 5 | 5
Instruction pipeline length | n.a. | 9 | 10 | 11
OoO Execution Window | 768 2x384 | 640 (2x 320) | 576 (2x 288) | 448 (2x 224)
Integer Execution Units | 8x ALU (6 SX + 2 MX) | 6x ALU (4 SX + 2 MX) | 4x ALU (2 SX + 2 MX) | 4x ALU (2 SX + 2 MX)
FP/SIMD Execution Units | 4 | 4 | 4 | 4
Branch Units | 3 | 2 | 2 | 2
L1 cache | 64KB | 64KB | 64KB | 64KB
L2 cache | Up to 2MB | 512KB / 1MB | 512KB / 1MB | 512KB / 1MB
SX ALU: Single-cycle ALU MX ALU: Multi-cycle ALU (for Mul. od Div.)
Evolution of key features of Cortex-X cores [79]

## Slide 192: 3.6 Armv9-A based 64-bit Cortex-A CPUs (45)
Widening the core width of ARM’s Cortex-X cores
The preceding Table indicates that ARM has made significant improvements to the
width of their high-performance Cortex X cores.
While the front end of the Cortex-X1 core (released in 2020) was only 5 wide, the
Cortex-X3 (released in 2022) became already 6 wide, and the Cortex-X4 (2023)
is expected to be 10 wide, assuming the source of this information is accurate.
 | X1-based DSU | TCS21 DSU110 | TCS22 Updated DSU110 | TCS23 DSU120
Cortex-X | X1 | X2 | X3 | X4
Core width | 5 | 5 | 6 | 10?
Table: Increasing the core width of the Cortex-X cores

## Slide 193: 3.6 Armv9-A based 64-bit Cortex-A CPUs (46)
Source: Unconfirmed forum message (https://x.com/Cardyak) from 06/2023.
Assumed block diagram of ARM’s Cortex-X4 CPU core indicating a 10-wide
CPU core

## Slide 194: 3.6 Armv9-A based 64-bit Cortex-A CPUs (47)
 | Uplift achieved by the cores vs. the previous implementation |  | 
Platform | Cortex-X-series cores in performance | Cortex-A700-series cores in efficiency | Cortex-A500-series cores in efficiency
TCS21 | 30 % | 30 % | 35 %
TCS22 | 22 % | 20 % | -5 %
TCS23 | 15 % | 20 % | 22 %
Cumulated uplift | 1.82x | 1.87x | 1.56x
How much performance and efficiency uplift has AMD achieved with the cores of the
introduced TCS platforms vs. previous implementations? [58], [79], [61]
Remarks
At first glance, it is surprising that the updated Cortex-A510 core module of the
TCS22 platform is 5% less efficient than its predecessor (initial Cortex-A510).
This can be attributed to the fact that the updated A510 core module provides support
for both the AArch32 and AArch64 execution modes, whereas the previous core module
(initial A510) only supports the AArch64.

## Slide 195: 3.6 Armv9-A based 64-bit Cortex-A CPUs (48)
Evolution of the width of mobile CPU cores -1
It is now challenging to compare the core widths of mobile CPU cores used in
smartphones and tablets.
The next two Figures present this comparison.

## Slide 196: 3.6 Armv9-A based 64-bit Cortex-A CPUs (49)
Evolution of the width of mobile CPU cores -1
3-wide
2-wide
4-wide
Width of mobile cores
(or of big cores of big.little or dynamIQ core clusters)
5-wide
ARM
v7 Cortex-A (2005-09)
(except 1-wide LP A5 (2009)
and 3-wide HP A15))
v7 HP Cortex-A15
(2010)
Intel
Atom family (2008-15)
AMD
Cat family (2011-2015)
Apple
v7 Cortex-A8 (2009)
v7 Swift (A6) (2012)
Qualcomm
v7 Scorpion
(S1-S3) (2007-10)
v7 Krait
(S4/S400/S60x/S80x)
(2012-14)
v8 Kryo/Kryo 280
(S820/821/835) (2015/2016/2017)
v8.2 Kryo 385
(S845) (2018)
Samsung
v8.0 M1 (2016)
(Exynos 8 Octa)
v8 M2 (2017)
(Exynos 9 Octa)
v8.0 HP Cortex-A (2013-15) (except 2-wide HP Cortex-A73)
v7 Exynos 5
(2013-14)
v8 Exynos 7
(2016)
v8.2 HP Cortex-A76
(2018) to
HP Cortex-A78
(2020)
HP: High-Performance/big core
LP: Low-Power
v8.0 HP Cortex-A73
(2016)
Airmont-based Atom core (2016)
v8.0/8.2 LP Cortex-A
(2013/2017)
v8.2 HP Cortex-A75
(2017)
v8.2 HP Cortex-X1
(2020))

## Slide 197: 3.6 Armv9-A based 64-bit Cortex-A CPUs (50)
Evolution of the width of mobile CPU cores -2
6-wide
7-wide
Width of mobile cores
(or of big cores of big.little or dynamIQ core clusters)
8-wide
ARM
Intel
AMD
Apple
Qualcomm
Samsung
HP: High-Performance/big core
LP: Low-Power
v8.0 HP A7-A10X
(2013-2017)
v8.2 HP A11 (2017)
v8.3 HP A12/A12X
(2018)
v8.4 HP A13 (2019)
v8.5 HP A14/M1
(2020)
v8.2 M6
(2020)/cancelled
v8.2 M3 (2018) Exynos 9810)
v8.2 M4 (2019) Exynos 9820)
v8.2 M5 (2019) Exynos 990)
v9.0 HP Cortex-X3
(2022)
10-wide
v9.2 HP Cortex-X4?
(2023)

## Slide 198: 3.6 Armv9-A based 64-bit Cortex-A CPUs (51)
Evolution of the width of mobile of CPU cores -3
As shown in the above Figures, by widening the front-end of the X4 core to 10,
ARM could catch up with Apple’s M4 core,bassuming that the cited source is correct

## Slide 199: 3.6 Armv9-A based 64-bit Cortex-A CPUs (52)
Use of Armv9-A based cores in mobile processors
Apple
Samsung
Exynos
Qualcomm
Snapdragon
Huawei
Kirin
MediaTek
2200 (2022)
(1+3+4)C
8 Gen 1 (2022)
(1+3+4)C
Dimensity 9000 (1+3+4)C (2021)
ARM
HP: Cortex-X2 (64-bit)
MS: Cortex-A710 (32/64-bit)
LP: Cortex-A510. (64-bit)
Armv9.0-A based
DynamIQ core clusters
(2021-)
HP: Cortex-X3 (64-bit)
MS: Cortex-A715 (64-bit)
LP: Cortex-A510 v2 32/64-bit)
(2022-)
Dimensity 9200 (1+3+4)C (2022)
8 Gen 2 (2022)
(1+4+3)C
HP: Cortex-X4 (64-bit)
MS: Cortex-A720 (64-bit)
LP: Cortex-A520 64-bit)
(2023-)
Armv9.2-A based
DynamIQ core clusters
Armv9-A based DynamIQ core clusters
8 Gen 3 (2023)
(1+5+2)C
Dimensity 9300 (4+4+0)C (2023)
M4 (2024)
(4+6)C

## Slide 200
3.7 Case example: The core complex of the TCS22 platform
(Optional reading, not a part of the Lecture.
It is included in the Annex.)

## Slide 201
3.8 Summing up: Main evolution steps of Armv7 to Armv9-based CPU designs in mobile processors

## Slide 202: 3.8 Main evolution steps of Armv7-v9 based CPU designs in mobile processors (1)
Single-core
CPUs
(≈2007-2012)
Cortex-A8
Typical Armv7 CPUs
Armv7-based 32-bit CPU designs in mobile processors
When and how have Armv7-based CPUs appeared in mobile devices?
During the second half of the 2000s, an increasing number of vendors began
incorporating the Cortex-A8 CPU in their smartphones.
The Cortex-A8 CPU was a single-core design.
Next, single-core designs became widely used, as shown in the next Figure.
This led to ARM’s dominance in mobile processors.
3.8 Summing up: Major evolution steps of Armv7 to Armv9-based CPU designs
in mobile processors

## Slide 203: 3.8 Main evolution steps of Armv7-v9 based CPU designs in mobile processors (2)
Single-core
processors
Armv7-A
CPUs
Cortex-A8 (~2007)
Apple
Samsung
Exynos
Qualcomm
Snapdragon
Huawei
Kirin
MediaTek
APL2298 1C (2009)
QSD8250 1C (2007)
(A8-based Scorpion core)
3110 1C (2010)
MT6515 1C (2012)
MT6575 1C (2012)
(both Cortex-A9 based)
Armv7-based 32-bit single-coreCPU designs in mobile processors
Emergence of single-core Armv7-based 32-bit CPUs in mobile processors -2

## Slide 204: 3.8 Main evolution steps of Armv7-v9 based CPU designs in mobile processors (3)
Evolution of ARM’s Cortex-A based CPUs in mobile processors
Since their emergence, nearly two decades ago, ARM’s Cortex-A-based mobile
processors have evolved tremendously.
This impressive evolution occurred in four major steps, which will be discussed
subsequently.

## Slide 205: 3.8 Main evolution steps of Armv7-v9 based CPU designs in mobile processors (4)
Transition from Armv7-based single-core 32-bit CPUs to Armv7-based 32-bit symmetrical multicores
ARM CPUs
ARM ISA
Apple
Samsung
Exynos
Qualcomm
Snapdragon
Huawei
Kirin
MediaTek
Processors
32-bit symmetrical
multicores
Cortex-A5/A8/A9
A5 (2011)
(2C)
4412 4C (2012)
7 7580 2x4C (2015)
8260 2C (2013)
400 4C (2013)
(K3V2 4C (2012)
620 2x4C (2014)
MT6582 4C (2013)
MT6592 2x4C (2013)
CC interconnect
Armv7
32-bit single-core
processors
Armv7-A
Cortex-A8 (~2007)
APL2298 1C (2009)
QSD8250 1C (2007)
(A8-based Scorpion core)
3110 1C (2010)
MT6515 1C (2012)
MT6575 1C (2012)
The first major evolution step: transitioning from single-core Armv7-based
32-bit CPUs to 32-bit symmetrical multicores -1

## Slide 206: 3.8 Main evolution steps of Armv7-v9 based CPU designs in mobile processors (5)
Apple A5 (2011)
Samsung 4412 (2012)
Qualcomm 8260 (2013)
Huawei K3V2 (2012)
MediaTek MT6582 (2013)
Apple A7 (2013)
Samsung E7 7580 (2015)
Qualcomm 410 (2015)
Huawei 620 (2014)
MediaTek MT6735 (2015)
Apple A10 (2016)
Samsung E8 8890 (2016)
Qualcomm 439 (2018)
Huawei 650 (2016)
MediaTek MT6750 (2016)
Armv7 32-bit symmetrical
multicore CPU
Armv8.0 64-bit big.little
CPU
Armv8.0 64-bit Symmetrical
multicore CPU
The second major step: transitioning from Armv7-based 32-bit symmetrical multicores
to Armv8.0-based 64-bit big.little CPUs -1
This transfer, however, occurred along two alternative paths in two steps.
Along one path
Armv7-based 32-bit symmetrical multicore CPUs were first transitioned to
Armv8.0-based 64-bit symmetrical multicore CPUs, and subsequently,
Armv8.0 64-bit symmetrical multicores were transitioned to Armv8.0 64-bit
big.little CPUs,
as illustrated below.

## Slide 207: 3.8 Main evolution steps of Armv7-v9 based CPU designs in mobile processors (6)
Samsung 4412 (2012)
Huawei K3V2 (2012)
MediaTek 6582 (2013)
Samsung 5410 (2013)
Huawei 920 (2014)
MediaTek MT8135 (2013)
Samsung E. 8 8890 (2016)
Huawei 650 (2016)
MediaTek MT6750 (2016)
Armv7 32-bit symmetrical
multicore CPU
Armv8.0 64-bit big.little
CPU
Armv7 32-bit
big.little
CPU/
The second major step: transitioning from Armv7-based 32-bit symmetrical
multicores to Armv8.0-based 64-bit big.little CPUs -2
Armv7-based 32-bit symmetrical multicore CPUs were first transitioned to
Armv7-based 32-bit big.little CPUs, and subsequently,
the Armv7-based 32-bit big.little CPUs were transitioned to Armv8.0 64-bit
big.little CPUs,
as illustrated below.
Along the another path

## Slide 208: 3.8 Main evolution steps of Armv7-v9 based CPU designs in mobile processors (7)
Apple A5 (2011)
Samsung 4412 (2012)
Qualcomm 8260 (2013)
Huawei K3V2 (2012)
MediaTek MT6582 (2013)
Samsung 4412 (2012)
Huawei K3V2 (2012)
MediaTek 6582 (2013)
Apple A7 (2013)
Samsung E7 7580 (2015)
Qualcomm 410 (2015)
Huawei 620 (2014)
MediaTek MT6735 (2015)
Apple A10 (2016)
Samsung E8 8890 (2016)
Qualcomm 439 (2018)
Huawei 650 (2016)
MediaTek MT6750 (2016)
Samsung 5410 (2013)
Huawei 920 (2014)
MediaTek MT8135 (2013)
Samsung E. 8 8890 (2016)
Huawei 650 (2016)
MediaTek MT6750 (2016)
Armv7 32-bit symmetrical
multicore CPU
Armv8.0 64-bit big.little
CPU
Armv8.0 64-bit Symmetrical
multicore CPU
Armv7 32-bit
big.little
CPU/
The two alternative paths for transitioning from Armv7-based 32-bit symmetrical
multicores to Armv8.0-based 64-bit big.little CPUs along two alternative paths

## Slide 209: 3.8 Main evolution steps of Armv7-v9 based CPU designs in mobile processors (8)
The reasoning why the second major evolution step occurred along two steps
The reason for transitioning CPU designs from Armv7-based 32-bit symmetrical
multicores to Armv8.0-based 64-bit big.little designs in two steps is, to reduce
the huge complexity and minimize the risk associated with introducing two new
technologies (64-bit and big.little architectures) simultaneously.
This approach is reminiscent of Intel’s Tik-Tok development model, where a given Core processor generation is transitioned to a scaled-down design with a new microarchitecture in two consecutive steps, as detailed in the related Chapter.

## Slide 210: 3.8 Main evolution steps of Armv7-v9 based CPU designs in mobile processors (9)
ARM cores
ARM ISA
Apple
Samsung
Exynos
Qualcomm
Snapdragon
Huawei
Kirin
MediaTek
Processors
HP: Cortex-A57/
A72/A73
LP: A53
Armv8.0
A10 (2016)
(2+2)C (Armv8.1)
8 8890 (2016)
(4+4)C
439 (2018)
(4 +4)C
650 (2016)
(4+4)C
MT6750 (2016)
(4+4)C
64-bit big.little
core clusters
CC interconnect
DynamIQ
core clusters
HP: Cortex-A75/A76/
A77/A78/X1
LP: A55
Armv8.2
9810 (2018)
(4+4)C
845 (2018)
(4+4)C
980 (2018)
(2+2+4)C
Helio P90 (2+6)C (2019)
A11 (2017)
(2+4)C
CC interconnect
The third major evolution step: transitioning from Armv8.0-based 64-bit
big.little CPUs to Armv8.2-based DynamIQ core clusters-based CPUs -1
Replacing Armv8.0-based 64-bit big.little CPUs by Armv8.2-based DynamIQ core clusters-based CPUs

## Slide 211: 3.8 Main evolution steps of Armv7-v9 based CPU designs in mobile processors (10)
The third major evolution step: transitioning from Armv8.0-based 64-bit
big.little CPUs to Armv8.2-based DynamIQ core clusters-based CPUs -2
As shown in the previous Figure, Armv8.0-based 64-bit big.little CPUs were replaced
by Armv8.2-based DynamIQ core clusters-based CPUs around 2017/2018.

## Slide 212: 3.8 Main evolution steps of Armv7-v9 based CPU designs in mobile processors (11)
DynamIQ
core clusters
Armv9-A based
DynamIQ core clusters
ARM cores
ARM ISA
Armv8.2
Armv9.0
Apple
Samsung
Exynos
Qualcomm
Snapdragon
Huawei
Kirin
MediaTek
9810 (2018)
(4+4)C
845 (2018)
(4+4)C
980 (2018)
(2+2+4)C
Helio P90 (2+6)C (2019)
2200 (2022)
(1+3+4)C
8 Gen 1(2022)
(1+3+4)C
A11 (2017)
(2+4)C
Processors
Dimensity 9000 (1+3+4)C (2021)
CC interconnect
CC interconnect
The fourth major evolution step: transitioning from Armv8.2-based DynamIQ
core clusters to Armv9.0-based DynamIQ core clusters -1
Replacing Armv8.2-based DynamIQ core clusters by Armv9.0-based DynamIQ core clusters
HP: Cortex-A75/A76/
A77/A78/X1
LP: A55
HP: Cortex-X2
MS: A-710
LP: A-510
M4 (2024)
(4+6)C

## Slide 213: 3.8 Main evolution steps of Armv7-v9 based CPU designs in mobile processors (12)
The fourth major evolution step: transitioning from Armv8.2-based DynamIQ
core clusters to Armv9.0-based DynamIQ core clusters -2
The preceding Figure marks the final step of the evolution of mobile CPUs (as of 07/2024).
It indicates that the Armv8.2-based DynamIQ core cluster-based CPUs were replaced
by Armv9-based DynamIQ core clusters-based CPUs around 2022.

## Slide 214: 3.8 Main evolution steps of Armv7-v9 based CPU designs in mobile processors (13)
Section 3.3
Section 3.5
Section 3.6
Cortex-A8
(~2007-10) ~2011-13)
Cortex-A57/A53
(~2016)
Cortex-A75/A55
(~2017-2019)
Cortex-X2/A710/A510
(~2021-2022)
First CPUs
Summing up: The main evolution path of Cortex-A based CPUs
Section 3.4
Figure: Main evolution paths of Armv7 to Armv9.0-based Cortex-A CPUs
based on
the Armv7-A ISA
Cortex-A CPUs
based on
the Armv8.0-A ISA
based on
the Armv8.2-A ISA
based on
the Armv9-A ISA
CC interconnect
CC interconnect
CC interconnect
CC interconnect
Along with the four evolution steps, the main evolution paths of Armv7 to Armv9.0-based
CPUs used in mobile processors stands out as follows:
64-bit
big.little CPUs
Single-core CPUs
then
32-bit symmetrical
multicore CPUs
DynamIQ
core clusters
based CPUs
Armv9 DynamIQ
core clusters
based CPUs

## Slide 215: 3.8 Main evolution steps of Armv7-v9 based CPU designs in mobile processors (14)
Remark [86]
The SPEC CPU 2017 benchmark package is SPEC's next-generation, industry-standard
CPU-intensive suite for comparing performance, while stressing the CPU, memory
subsystem, and compiler.
Comparing the performance of current mobile processors
It is worth comparing the performance of current mobile processors with each
other and in relation to client processors.
A recent publication [87] makes this comparison easy by revealing SPECint2017
performance scores for c/c++ workloads, average power consumption [in W]
and the energy consumed during benchmark measurement [in Joule] for
current mobile processors (see the next Figure).

## Slide 216: 3.8 Main evolution steps of Armv7-v9 based CPU designs in mobile processors (15)
Performance (measured in SPECint2017 (c/c++) scores), average power (in W)
and energy consumption (in Joule) of current mobile processors [87] -1
S: Snapdragon (Qualcomm)
E: Exynos (Samsung)
D: Dimensity (MediaTek)
GS101 (Google)

## Slide 217: 3.8 Main evolution steps of Armv7-v9 based CPU designs in mobile processors (16)
Performance (measured in SPECint2017 (c/c++) scores), average power (in W)
and energy consumption (in Joule) of current mobile processors [87] -2
The cited results demonstrate that Apple’s A14 and A15 big cores provide
exceptional performance.
Qualcomm’s X2 cores, included in Snapdragon 8 gen 1 processors, deliver the
next highest performance, while the X1 cores of their Snapdragon processors
offer slightly less performance.
Note that Samsung’s’ or MediaTek’s A77 or A78-based cores show comparable but lower performance.
It’s important to note that the large cores of Apple's A14 and A15 processors already exhibit similar performance levels to Intel’s and AMD's client processors.
However, client processors consume significantly more power, with a TDP of
around 100 W.

## Slide 218
4. References

## Slide 219
4. References (1)
[2]: Greenhalgh P., big.LITTLE Processing with ARM Cortex-A15 & Cortex-A7, White Paper,
Sept. 2011, http://www.arm.com/files/downloads/big_LITTLE_Final_Final.pdf
[3]: Cortex-A73 Processor, ARM,
https://www.arm.com/products/processors/cortex-a/cortex-a73-processor.php
[4]: The Samsung Exynos 7420 Deep Dive – Inside A Modern 14nm SoC, June 29 2015,
http://monimega.com/blog/2015/06/29/the-samsung-exynos-7420-deep-dive-inside-a-
modern-14nm-soc/
[5]: Hsu D., ARM Cortex-A75 and Cortex-A55, ARM Tech Forum, Shenzen, Jun. 14, 2017,
https://docplayer.net/85228086-Arm-cortex-a75-and-cortex-a55.html
[6]: ARM Q4 2016 Roadshow Slides, ARM Holdings, 2017
file:///C:/Users/sima/Downloads/ARM_SB_Q4_2016_Roadshow_Slides_FINAL.pdf
[7]: Stephens N., Armv8-A Next-Generation Vector Architecture for HPC, Hot Chips 2016,
https://community.arm.com/groups/processors/blog/2016/08/22/technology-update-
the-scalable-vector-extension-sve-for-the-armv8-a-architecture
[8]: Architecture and Implementation of the ARM Cortex-A8 Microprocessor, Design & Reuse,
http://www.design-reuse.com/articles/11580/architecture-and-implementation-of-the-
arm-cortex-a8-microprocessor.html
[9]: Frumusanu A., ARM Details Built on ARM Cortex Technology License, AnandTech,
May 29 2016, https://www.anandtech.com/show/10366/arm-built-on-cortex-license
[1]: Cult of Mac, https://www.cultofmac.com/?utm_content=cmp-true

## Slide 220
4. References (2)
[10]: Rao A., ARM: a mandatory primer, Element14, 2014
[11]: https://www.statista.com/statistics/1131983/arm-based-chip-unit-shipments-as-reported-by-licensees-worldwide/
[12]: Shilov A.; Over 200 Billion Arm-Based Chips Shipped;tomshardware.com; October 20, 2021; https://www.tomshardware.com/news/over-200-billion-of-arm-chips-shipped
[15]: Levy M., The History of The ARM Architecture: From Inception to IPO,
http://www.reds.ch/share/cours/ReCo/documents/TheHistoryOfTheArmArchitecture.pdf
[13]: The ARM Architecture, http://www.eng.auburn.edu/~strouce/DaTseminar/UniPres07s.pdf
[14]: Wikipedia, ARM architecture, http://en.wikipedia.org/wiki/ARM_architecture
[16]: http://reds.heig-vd.ch/share/cours/reco/documents/thehistoryofthearmarchitecture.pdf
[17]: Quested T., ARM scales up again in Cambridge, Businessweekly, 20 October, 2014,
http://www.businessweekly.co.uk/news/property-and-construction/17695-arm-scales-
again-cambridge#sthash.Pzg7jnpK.dpuf
[18]: NVIDIA and SoftBank Group Announce Termination of NVIDIA’s Acquisition of Arm Limited; nvidianews; February 7. 2022.; https://nvidianews.nvidia.com/news/nvidia-and-softbank-group-announce-termination-of-nvidias-acquisition-of-arm-limited
[19]: Batten C., ECE 4750 Computer Architecture Intel Skylake, https://www.csl.cornell.edu/courses/ece4750/2016f/handouts/ece4750-section-skylake.pdf

## Slide 221
4. References (3)
[20]: Arm® Architecture Reference Manual for A-profile architecture ARM DDI 0487H.a (ID020222), 2022
[21]: Lemieux J., Introduction to ARM thumb, Embedded, Sept. 24 2003, http://www.embedded.
com/electronics-blogs/beginner-s-corner/4024632/Introduction-to-ARM-thumb
[22]: ARM Architecture Reference Manual, Armv8, 2013, http://www.myir-tech.com/down/arm/
arch/Armv8-A_Architecture_Reference_Manual_%28Issue_A.a%29.pdf
[23]: Eyrolles N., TEE and trust: assessing the security of Arm’s TrustZone, Viaccess-orca,
Febr. 17 2021, https://www.viaccess-orca.com/blog/assessing-the-security-of-arms-trustzone
[24]: Intel 64 and IA-32 Architectures Software Developer’s Manual Volume 1: Basic
Architecture, Order Number: 253665-067US, May 2018,
http://kib.kiev.ua/x86docs/SDMs/253665-067.pdf
[25]: Lomont C., Introduction to Intel Advanced Vector Extensions, Intel, 23 May 2011,
https://software.intel.com/sites/default/files/m/d/4/1/d/8/Intro_to_Intel_AVX.pdf
[26]: Frumusanu A.; Arm Announces Neoverse V1, N2 Platforms & CPUs, CMN-700 Mesh: More Performance, More Cores, More Flexibility; anadetech.com; April 27. 2021.; https://www.anandtech.com/Show/Index/16640?cPage=4&all=False&sort=0&page=5&slug=arm-announces-neoverse-v1-n2-platforms-cpus-cmn700-mesh
[27]: ARM Architecture Reference manual Supplement - The Scalable Vector Extension (SVE),
for Armv8-A, ARM DDI 0584Ab (ID081717), 21 Aug. 2017,
https://developer.arm.com/docs/ddi0584/latest/arm-architecture-reference-manual-
supplement-the-scalable-vector-extension-sve-for-armv8-a

## Slide 222
4. References (4)
[28]: Introduction to SVE, 2021, 102476_0001_00_en_introduction-to-sve.pdf
[29]: ARM Teaching Material, http://www.arm.com/files/ppt/ARM_Teaching_Material.ppt
[30]: Snyder C.D., ARM Family Expands at EPF, ARM11 Microarchitecture Stretches Pipe to Boost
Frequency, Microprocessor, June 3 2002
[31]: Cormie D., The ARM11 Microarchitecture, April 2002
https://www.hashimi.ws/cs214/ref_doc/ARM11%20Microarchitecture%20White%20Paper.
pdf
[32]: Hirata K., ARM11 MPCore, The streamlined and scalable ARM11 processor core, Jan. 2007,
http://www.aspdac.com/aspdac2007/pdf/archive/7D-2.pdf
[33]: ARM Cortex Application Processors, http://www.arm.com/products/processors/index.php
[34]: ARM SecurCore Processors, http://www.arm.com/products/processors/securcore/index.php
[35]: ARM® Architecture Reference Manual Armv8, for Armv8-A architecture profile,
ARM DDI 0487A.k_iss10775 (ID092916),2013-2016
https://silver.arm.com/download/ARM_and_AMBA_Architecture/AR150-DA-70000-r0p0-
01eac1/DDI0487A_k_armv8_arm_iss10775.pdf
[36]: Goodacre J., The Evolution of the ARM Architecture Towards Big Data and the Data-Centre,
8th Workshop on Virtualization in High-Performance Cloud Computing (VHPC’13),
Nov. 17-22 2013, http://www.virtical.eu/pub/sc13.pdf

## Slide 223
4. References (5)
[37]: L. Shimpi A., ARM's Cortex A7: Bringing Cheaper Dual-Core & More Power Efficient High-End Devices, https://www.anandtech.com/, October 19, 2011, https://www.anandtech.com/show/4991/arms-cortex-a7-bringing-cheaper-dualcore-more-power-efficient-highend-devices
[38]: Klug B.; Samsung Galaxy Note 2 Review (T-Mobile) - The Phablet Returns; anandtech.com; 24. October 2012.; https://www.anandtech.com/show/6386/samsung-galaxy-note-2-review-t-mobile-/3
[39]: Schor D., Intel Launches 10th Gen Comet Lake Desktop Processors, WikiChip Fuse 20 Apr., 2020, https://fuse.wikichip.org/news/3466/intel-launches-10th-gen-comet-lake-desktop-processors/
[40]: Katouzian A., The Qualcomm difference, 2013,
https://www.qualcomm.com/media/documents/files/the-qualcomm-difference.pdf
[41]: ARM, big.LITTLE Technology, 2014,
http://www.arm.com/products/processors/technologies/biglittleprocessing.php
[42]: Jeff B., Advances in big.LITTLE Technology for Power and Energy Savings, White Paper,
Sept. 2012, http://www.arm.com/files/pdf/Advances_in_big.LITTLE_Technology_for_
Power_and_Energy_Savings.pdf
[43]: big.LITTLE MP, Linaro, https://wiki.linaro.org/projects/big.LITTLE.MP#Overview
[44]: Variable SMP – A Multi-Core CPU Architecture for Low Power and High Performance, Nvidia, Whitepaper, 2011, http://www.nvidia.com/content/PDF/tegra_white_papers/tegra whitepaper-0911b.pdf

## Slide 224
4. References (6)
[45]: Greenhalgh P., Big.LITTLE Processing with ARM Cortex-A15 & Cortex-A7, White Paper,
Sept. 2011, http://www.arm.com/files/downloads/big.LITTLE_Final.pdf
[46]: Randhawa R., ARM's big.LITTLE systems provide more processing power for less energy,
New Electronics, July 10 2012, http://www.newelectronics.co.uk/electronics-technology/
arms-big-little-systems-provide-more-processing-power-for-less-energy/43563/
[48]: Frumusanu A., Arm Announces Armv9 Architecture: SVE2, Security, and the Next Decade,
AnandTech, March 30 2021, https://www.anandtech.com/print/16584/arm-announces-
armv9-architecture
[49]: Arm DynamIQ: Technology for the next era of compute, ARM Community,
https://community.arm.com/processors/b/blog/posts/arm-dynamiq-technology-for-the-
next-era-of-compute
[47]: Crijns K., ARM: 20 dollar and 64-bit Android smartphones to be expected, Hardware.info,
June 24 2014, http://us.hardware.info/reviews/5386/2/arm-20-dollar-and-64-bit-android-
smartphones-to-be-expected-android-64-bitn
[50]: Triggs R., Everything you need to know about ARM’s DynamIQ, Android Authority,
May 29, 2017, https://www.androidauthority.com/arm-dynamiq-need-to-know-770349/
[52]: Greenhalgh P., ARM DynamIQ. Intelligent Solutions Using Cluster Based Multiprocessing,
Hot Chips 29, 2017 Aug. 12,
https://www.slideshare.net/ARMHoldings/arm-dynamiq-intelligent-solutions-using-
cluster-based-multiprocessing
[51]: Cortex-A73, ARM Developer,
https://developer.arm.com/products/processors/cortex-a/cortex-a73

## Slide 225
4. References (7)
[53]: I will take you to the past and present of the mobile phone ARM processor in minutes, no
longer have to worry about my wife and wife let me choose a mobile phone...,
Programmer Sought, https://www.programmersought.com/article/77841675152/
[54]: Walrath J., ARM Tech Day 2017: DynamIQ, Cortex-A55, A75, and Mali-G72,
PC Perspective, May 29, 2017,
https://www.pcper.com/reviews/General-Tech/ARM-Tech-Day-2017-DynamIQ-Cortex-A55-
A75-and-Mali-G72/Cortex-A75-and-Mali-G72
[55]: Frumusanu A., Arm Announces Mobile Armv9 CPU Microarchitectures: Cortex-X2, Cortex-A710
& Cortex-A510, AnandTech, May 25 2021, https://www.anandtech.com/print/16693/arm-
announces-mobile-armv9-cpu-microarchitectures-cortexx2-cortexa710-cortexa510
[56]: Bannister S., Memory Tagging Extension: Enhancing memory safety through architecture,
ARM Community, Aug. 5 2019, https://community.arm.com/developer/ip-products/
processors/b/processors-ip-blog/posts/enhancing-memory-safety
[57]: Armv8.5-A Memory Tagging Extension, White Paper;
[58]: Bedi A., ARM Community blogs, Architectures and Processors blog, The foundation of Total Compute: First Armv9 Cortex CPUs, https://community.arm.com/,May 25, 2021, https://community.arm.com/arm-community-blogs/b/architectures-and-processors-blog/posts/first-armv9-cpu-cores
[59]: Frumusanu A., Arm's New Cortex-A78 and Cortex-X1 Microarchitectures: An Efficiency and
Performance Divergence, AnandTech, May 26 2020,
https://www.anandtech.com/show/15813/arm-cortex-a78-cortex-x1-cpu-ip-diverging
[60]: Shimpi A.L., AMD Discloses Bobcat & Bulldozer Architectures at Hot Chips 2010, AnandTech,
Aug. 24 2010, https://www.anandtech.com/show/3863/amd-discloses-bobcat-bulldozer-
architectures-at-hot-chips-2010

## Slide 226
4. References (8)
[61]: The Armv9 CPU Compute Foundation for TCS23, May 29, 2023, https://images.anandtech.com/doci/18871/Arm%20Client%20Tech%20Days%20CPU%20Presentation_Final-12.png
[62]: McGregor J.; Arm Upgrades Its Entire Portfolio of Pc and Mobile IP; eetasia.com; 31. May 2021.; https://www.eetasia.com/arm-upgrades-its-entire-portfolio-of-pc-and-mobile-ip/
[63]: An Introduction to the Intel® QuickPath Interconnect, January 2009; https://www.intel.com/content/www/us/en/io/quickpath-technology/quick-path-interconnect-introduction-paper.html/
[64]: https://studfile.net/preview/9178230/page:5/
[65]: Intel 64 and IA-32 Architectures Software Developer’s Manual Volume 1: Basic
Architecture, Order Number: 253665-067US, May 2018,
http://kib.kiev.ua/x86docs/SDMs/253665-067.pdf
[66]: Shimpi A.L., The ARM Diaries, Part 2: Understanding the Cortex A12, AnandTech,
July 17 2013, http://www.anandtech.com/show/7126/the-arm-diaries-part-2-
understanding-the-cortex-a12
[67]: Schor D.; Intel Rolls Out 13th Gen Core, Raptor Lake Processors; Cranks Up The Frequency, https://fuse.wikichip.org/; October 1, 2022, https://fuse.wikichip.org/news/7149/intel-rolls-out-13th-gen-core-raptor-lake-processors-cranks-up-the-frequency/
[68]: Rahman J.; Intel CPU Die Topology, https://jprahman.substack.com/; May 28, 2023, https://jprahman.substack.com/p/intel-cpu-die-topology

## Slide 227
4. References (9)
[69]: Aufranc J-L., Arm unveils Cortex-X3 and Cortex-A715 Armv9 cores, improves Cortex-A510 efficiency, https://www.cnx-software.com/, Jun 29, 2022, https://www.cnx-software.com/2022/06/29/arm-cortex-x3-cortex-a715-armv9-cores-improves-cortex-a510-efficiency/
[70]: Dipert B., AMD’s Barcelona: Quad-Core Opteron unveiled, https://www.edn.com/, September 11, 2007, https://www.edn.com/amds-barcelona-quad-core-opteron-unveiled/
[71]: Shimpi A.L., Intel's Sandy Bridge Architecture Exposed, September 14, 2010, https://www.anandtech.com/show/3922/intels-sandy-bridge-architecture-exposed/4
[72]: Kottapali S., Baxter J., “Nehalem-EX CPU Architecture”, Hot Chips 21, 2009,
http://www.hotchips.org/archives/hc21/2_mon/HC21.24.100.ServerSystemsI-Epub/
HC21.24.122-Kottapalli-Intel-NHM-EX.pdf
[73]: Morgan T. P., Intel Puts More Compute Behind Xeon E7 Big Memory, The Platform,
May 5 2015, http://www.theplatform.net/2015/05/05/intel-puts-more-compute-behind-
xeon-e7-big-memory/
[74]: Schor D.; Arm Launches New Coherent And SoC Interconnects: CI-700 & NI-700, https://fuse.wikichip.org/; May 25, 2021, https://fuse.wikichip.org/news/5271/arm-launches-new-coherent-and-soc-interconnects-ci-700-ni-700/
[75]: Shimpi A.L., ARM Cortex A17: An Evolved Cortex A12 for the Mainstream in 2015,
AnandTech, Febr. 11 2014, http://www.anandtech.com/show/7739/arm-cortex-a17
[76]: https://www.quora.com/, In your perspective, is there possible relationship between the processor and the display quality of your device?, https://www.quora.com/In-your-perspective-is-there-possible-relationship-between-the-processor-and-the-display-quality-of-your-device

## Slide 228
4. References (10)
[77]: Kinjal D., How Arm’s Total Compute solutions will power the next decade of compute, https://community.arm.com/, May 25, 2021, https://community.arm.com/arm-community-blogs/b/architectures-and-processors-blog/posts/total-compute-solutions
[78]: Pradhan S., ARM Community blogs, Architectures and Processors blog, Arm Cortex-X4 advances frontiers of CPU performance, https://community.arm.com/, May 29, 2023, https://community.arm.com/arm-community-blogs/b/announcements/posts/cortex-x4-cpu-performance
[79]: Triggs R., Arm Cortex-X3 and Cortex-A715: Next-gen CPUs redefined, https://www.androidauthority.com/, Apr 18, 2023, https://www.androidauthority.com/arm-cortex-x3-cortex-a715-3178608/
[80]: Geekerwan., 苹果M4性能分析：尽力了，但芯片工艺快到头了！https://www.youtube.com/, May, 2024, https://www.youtube.com/watch?v=EbDPvcbilCs
[81]: Hall C., Arm Cortex X3 Vc Cortex A715, https://trendblog.net/, Jun 29, 2022, https://trendblog.net/arm-cortex-x3-vc-cortex-a715/
[82]: Dave K., ARM Community blogs, Announcements, Arm Total Compute Solutions 2022: Supercharging visual experiences for next-generation devices, , https://community.arm.com/, Jun 28, 2022, community.arm.com/arm-community-blogs/b/announcements/posts/second-generation-arm-total-compute-solutions
[83]: Frumusanu A., Arm Announces Mobile Armv9 CPU Microarchitectures: Cortex-X2, Cortex-A710
& Cortex-A510, AnandTech, May 25 2021, https://www.anandtech.com/print/16693/arm-
announces-mobile-armv9-cpu-microarchitectures-cortexx2-cortexa710-cortexa510
[84]: Wikichip, https://en.wikichip.org/wiki/File:a510-decode.svg

## Slide 229
4. References (11)
[85]: Arm® DynamIQ™ Shared Unit-110 Technical Reference Manual, file:///C:/Users/NIK/Downloads/arm_dsu_110_trm_102639_0201_01_en.pdf
[86]: https://www.spec.org/cpu2017/
[87]: Cutress I., The Snapdragon 8 Gen 1 Performance Preview: Sizing Up Cortex-X2, AnandTech, Dec. 14, 2021, https://www.anandtech.com/show/17102/snapdragon-8-gen-1-performance-preview-sizing-up-cortex-x2/2
[88]: Reimer J., A history of ARM, part 3: Coming full circle, Arstechnics, Jan. 17, 2023,
https://arstechnica.com/gadgets/2023/01/a-history-of-arm-part-3-coming-full-circle/5/
[89]: Arm CoreLink CCI-500 Cache Coherent Interconnect Technical Reference Manual r1p0,
ARM Developer, Nov. 27, 2014,
https://developer.arm.com/documentation/100023/0100/functional-description/operation
/snoop-filter

## Slide 230
Annex
2.2 A closer look at the SVE register set-based ISA extensions
3.1 ARM’s CPU designs preceding the ARM Cortex family
3.7 Case example: The core complex of the TCS22 platform
(These Sections are optional readings,
they are not part of the Lecture)

## Slide 231
2.2 A closer look at the SVE register set-based ISA extensions
(Optional reading, not a part of the Lecture)

## Slide 232: 2.2.4 A closer look at the SVE register set-based ISA extensions (1)
2.2 A closer look at the SVE register set-based ISA extensions
To support FX/FP SIMD operations on long (up to 16x128-bit wide) data, ARM introduced
the SVE (Scalable Vector Extension) and SVE2 extensions in the Armv8.2 ISA in 2017.
It is based on the SVE register set, which is the third register set of the ARM ISA,
as indicated below.
Discussed in the previous Sections
Discussed in this Section
It supports
FX/ FX-SIMD operations
It supports
scalar FP/vector FP and
FX/FP SIMD operations
It supports
FX/FP SIMD operations
on long (up to 16x128-bit) data
Armv1/Armv6
Armv5/Armv7
Armv8.2
The GPR register set
The secondary register set
The SVE register set
Register sets provided by the Arm ISA
Introduced in
(1985/2002)
(2000/2005)
(2017)
Figure: The SVE register set

## Slide 233: 2.2.4 A closer look at the SVE register set-based ISA extensions (2)
The SVE register set
LEN: 1 to 16
The 1. lanes (first 128 bits) of the SVE Z register set are shared with the 32 128-bit
wide SIMD registers (V0-31) of the Armv8.0 ISA, as indicated below.
The SVE register set is comprised of 32 Z registers.
The length of the SVE registers is not fixed but implementation-dependent;
it matches the width of the SIMD execution units of the processor.
However, it should be a multiple of 128 bits (up to 16 x 128 = 2048 bits).
The specific size of the SVE registers is held in a field of a control register called
LEN, which is not discussed further here.
Designation of the SVE registers [7]

## Slide 234: 2.2.4 A closer look at the SVE register set-based ISA extensions (3)
Possible data elements per 128-bit lane [27]
8-bit FX
16-bit FX/FP
32-bit FX/FP
64-bit FX/FP
128-bit FX
Possible data elements
in the 128-bit lanes

## Slide 235: 2.2.4 A closer look at the SVE register set-based ISA extensions (4)
The SVE extension was introduced in the Armv8.2-A ISA in 2017 as an optional feature,
whereas the SVE2, which was launched in the Armv9-A ISA in 2021, is mandatory.
The SVE2 is a superset of SVE, i.e., it includes all instructions of the SVE.
Introduction of the SVE and SVE2 ISA extensions

## Slide 236: 2.2.4 A closer look at the SVE register set-based ISA extensions (5)
a) The SVE register set based SVE SIMD extension [7]
The SVE (Scalable Vector Extension) was announced in 2016 (at the Hot Chips
conference) and introduced in the Armv8.2-based ISA in 2017 as an optional feature.
SVE is implemented only in the AArch64 version of Armv8.2 and supports both
FX- and FP processing.
SVE is designed for HPC workloads rather than media or image processing.

## Slide 237: 2.2.4 A closer look at the SVE register set-based ISA extensions (6)
Key feature of the SVE extension: Vector length agnostic programming
As we discussed, both the x86 and Arm ISAs support increasingly wider SIMD
execution, such as 64-bit, 128-bit, 256-bit, and 512-bit long SIMD processing.
However, the x86 ISA extensions have a drawback since with each new extension,
such as MMX, SSE, SSE2, SSE3, AVX, AVX512, a further instruction subset is
introduced.
So, to utilize the benefits of wider and wider SIMD execution resources, software
had to be rewritten and recompiled.
By contrast, with the SVE extension, programming becomes "vector length agnostic,"
meaning the programmer no longer needs to use different instruction subsets
for different long ISA extensions.

## Slide 238: 2.2.4 A closer look at the SVE register set-based ISA extensions (7)
Interpretation of vector length agnostic programming [26]
As indicated in the Figure above, the same binary code runs on different wide
hardware, i.e. different wide SIMD execution units.
(implemented by masking)

## Slide 239: 2.2.4 A closer look at the SVE register set-based ISA extensions (8)
Benefits of vector length agnostic (VLA) programming
VLA simplifies programming, enabling binary code to be portable across different
processors with varying SIMD execution units, as instruction execution is
automatically scaled to match available resources.
A further advantage of vector-length agnostic programming is that it allows
for auto-vectorization by advanced compilers.
Auto-vectorization: automatically generates SIMD code from loops.

## Slide 240: 2.2.4 A closer look at the SVE register set-based ISA extensions (9)
How ARM implements data vector length agnostic programming? [28]
Up to 16x16 bit
Figure: Predicate registers
The introduced SVE extension utilizes Predicate registers (P registers) as masks
to indicate which active elements of the Z-registers are involved in the operation.
There exist 16 Predicate registers, as seen below.
P0-P7 include predicates for loads, stores, and arithmetic operations,
P8-P15 are extra predicates for loop management.
Predicate registers hold one bit for each byte available in a Z register.
For example, an implementation providing 1024-bit Z registers has 128-bit wide
Predicate registers.

## Slide 241: 2.2.4 A closer look at the SVE register set-based ISA extensions (10)
Predicate registers (1 bit for each byte) are used as masks for data operations.
A „1” value of the Predicate register will activate the associated byte, a „0” value
will neglect it.
The next example demonstrates this.
Specifying the word length (vector lengths) in the instructions -1

## Slide 242: 2.2.4 A closer look at the SVE register set-based ISA extensions (11)
Example: Masking out active data elements from the SVE-registers by
using predicates while performing the zo < z1 + z0 operation [28]
The active data elements of the source registers Z0 and Z1 (indicated by the
„1” values per byte in the Predicate register P0) are added and the result is
written into the destination register Z0.
The masked out data elements of the SVE source register Z0 are copied into
the destination register Z0.
1111
1111
0000
0000

## Slide 243: 2.2.4 A closer look at the SVE register set-based ISA extensions (12)
When writing programs, in addition to specifying the operation code and the source
and destination registers, it is necessary to also specify a previously set Predicate
register to identify the length of the data elements, i.e. to show which data elements
will be used in the referenced SVE registers.
Specifying the length of vectors (data words) in the instructions -2

## Slide 244: 2.2.4 A closer look at the SVE register set-based ISA extensions (13)
Remark
Our previous discussion of the use of Predicate registers is strongly simplified.
For a more detailed explanation we refer to [27] or [28].

## Slide 245: 2.2.4 A closer look at the SVE register set-based ISA extensions (14)
Speed-up potential of SVE [7]
As the above Figure indicates, SVE brings real speed-up only for appropriate workloads.

## Slide 246: 2.2.4 A closer look at the SVE register set-based ISA extensions (15)
b) The 2. generation 128 – 2048-bit FX/FP SIMD extension, called the
SVE2 ISA extension
The SVE2 extension was introduced in the Armv9-A ISA in 2021 as a mandatory feature.
While the previous SVE extension mainly focused on HPC (High-Performance Computing) workloads, the SVE2 extension provides a much broader range of instructions and can be seen as a potential successor to the recent SIMD extension, known as Neon.

## Slide 247: 2.2.4 A closer look at the SVE register set-based ISA extensions (16)
Each 128-bit lane holds: FX8/16/32/64
FP161/32/64
data elements
SVE (2017)/SVE2 (2021) extensions
Armv8.2 (AArch64 mode)
(optional)
128
32
SVE register set
Up to 16x 128-bit wide lanes
FX/FP SIMD (vector) data
---
Up to 16 x 128-bit (Up to 2048-bit)
Summing up the layout of the SVE register extensions (2017/2021)
1. lane
2. lane
15.lane
The data width must be multiples of 128 bits, up to 16x128-bit.
The 1. lanes (first 128 bits) of the SVE Z register set are shared with the 32 128-bit
wide SIMD registers (V0-31) of the Armv8.0 ISA.
1: Only data conversions are supported.

## Slide 248: 2.2.4 A closer look at the SVE register set-based ISA extensions (17)
Contrasting the SVE and SVE2 SIMD extensions
ARM ISA |  | ISA extension | The SVE register set based SIMD extensions |  |  | 
 |  |  | Available register set | Scalar data types | Vector data types | Instruction subset
Name | Year |  |  |  |  | 
Armv8.2 (optional) | 2017 | SVE | SVE register set 32 registers each (1...16)x128-bit wide | --- | FX 8/16/32/64/128 FP 16/32/64 (1...16)x128-bit wide SIMD data (FMA available) | Small basic instruction subset aiming at HPC workloads
Armv9 (superset of SVE) (mandatory) | 2021 | SVE2 |  |  |  | 
 |  |  |  |  |  | (Vastly enhanced instruction subset aiming at general-purpose workloads
HPC: High-Performance Computing
SVE2 is a superset of SVE.
It offers a wide range of instruction set extensions for faster and more efficient
execution of long SIMD data.
The execution resources provided for SVE/SVE2 instructions are 128-bit quantized,
meaning they may be 128-bit, 256-bit, etc., in length up to 2048-bit.

## Slide 249: 2.2.4 A closer look at the SVE register set-based ISA extensions (18)
Implementation of the SVE and SVE2 extensions in processors
On the other hand, SVE2 has been recently (2021) implemented in the
Armv9 ISA-based Neoverse and Cortex designs.
The SVE extension has been implemented only by Fujitsu in its A64FX processor so far.
The A64FX processor includes 48 cores, is based on the Arm8.2 ISA, and offers
512-bit wide SIMD execution.
It is manufactured using 7 nm technology and is incorporated in the Fugaku supercomputer, which was designed by Fujitsu and completed in 03/2021.
Implementing SVE in a supercomputer is not at all surprising, as SVE targets
HPC workloads, which are not typical on mobiles or tablets.

## Slide 250: 2.2.4 A closer look at the SVE register set-based ISA extensions (19)
Importance of the SVE and SVE2 ISA extensions
very wide (up to 16x128-bit) vector processing and
vector length agnostic programming,
(it refers to programming that is not dependent on the length of the
vectors used).
Further on, the SVE2 extension is expected to replace the previous 64/128-bit
FX/FP-SIMD extension (called Neon).
This is why we discuss these extensions in a separate Section.
These extensions have great importance since they allow

## Slide 251
3.1 ARM’s CPU designs preceding the ARM Cortex family
(Optional reading, not a part of the Lecture)

## Slide 252: 3.1 ARM’s CPU designs preceding the ARM Cortex family (1)
3.1 ARM’s CPU designs preceding the ARM Cortex family
a) Overview of Armv1-Armv2 based CPU cores and their use in mobiles [29]

## Slide 253: 3.1 ARM’s CPU designs preceding the ARM Cortex family (2)
Remarks to the address spaces supported
The earliest CPU cores, such as the ARM1 or ARM2 cores, were based on the ISA
versions Armv1 and Armv2 .
These cores only had a 26-bit address bus but a 32-bit data bus, which makes
them ARM’s 26-bit architectures.
On the other hand, CPU cores based on the Armv3 or higher ISA versions up to the
Arm v7 ISA already support a 32-bit address space and are referred to as 32-bit
architectures.
Later, the Armv8 ISA expanded the address space to 64-bit in the AArch64 mode,
paving the way for 64-bit architectures.
As already mentioned in Section 2.1:

## Slide 254: 3.1 ARM’s CPU designs preceding the ARM Cortex family (3)
ARM’s basic ISA (Armv3 – v4) [21], [22]
Stack pointer
Link register
PC
32-bit wide
GPRs in the Armv3-v7 ISA
R0
R1
R2
.
.
.
R12
R13(SP)
R14(LR)
R15(PC)
Scalar data
FX32
Boole32
Basic ISA
Basic register set
Note: Subsequently we do not follow the use of the Boolean data type.
b) Overview of Armv3 - Armv6 based CPU cores and their use in mobiles

## Slide 255: 3.1 ARM’s CPU designs preceding the ARM Cortex family (4)
Main extensions introduced in the Armv4 – Armv6 ISA versions (simplified)
Armv4
Armv5
Armv6
Armv8.0-A
Armv7-A
Jazelle
(Jazelle DBX)
VFPv1/2
Thumb6
(Armv4T)
SIMD
TrustZone
Thumb-2
(Armv6T2)
Adv. SIMD1
(NEON)
VFPv3/v42
Crypto-graph. extension
Jazelle
(ex. by SW)
Jazelle RCT3
(ThumbEE)
ARM710T
(~1995)
ARM10200
(2000)
ARM1136
(2002)
Cortex-A5 - A15
(2005)
Cortex-A53/A57
(2012)
To enhance
security
To speed up
the execution
of bytecodes
AArch32
AArch64
A32
AArch64
Armv9-A
Neoverse N2/V1
Cortex-X2/A510/A710
cores (2021)
A64
T32
(Thumb)
SVE4
(v8.2, opt.)
Confidential
Compute Arch.
MTE
A64
Aarch325
SVE2
To enhance
compute
capabilities
For the Remarks see the next slide.
The thumb instruction set aims at reducing code size.

## Slide 256: 3.1 ARM’s CPU designs preceding the ARM Cortex family (5)
1The Advanced SIMD architecture extension is commonly referred to as the
NEON technology.
2The VFP subset became depricated in the Armv8 ISA.
3Jazelle-RTC (ThumbEE) became depricated in Armv7 Issue C in 10/2011.
4The SVE (Scalable Vector Extension) subset became introduced in the
Armv8.2 ISA as an optional feature, only in 2017.
5The AArch32 execution mode is only supported in certain implementations, e.g.
for the Cortex-A510 CPU.
Explanation of the superscripts in the previous Figure

## Slide 257: 3.1 ARM’s CPU designs preceding the ARM Cortex family (6)
XScale is a trademark of Intel Corporation
Overview of ARM’s CPU cores implementing the Armv4 – Armv6 ISAs [29]
1998
2000
2002
2004
time
version
Armv5
Armv6
1994
1996
2006
ARMV4
StrongARM
ARM926EJ-S
XScale
ARM102xE
ARM1026EJ-S
ARM9x6E
ARM92xT
ARM1136JF-S™
ARM7TDMI-S
ARM720T
SC100
SC200
ARM1176JZF-S
ARM1156T2F-S
ARM1136JF-S™
Notes: Versions mostly refer to the instruction set that the ARM core executes.
The ARM7, which is still the most often used core in a low-power design, executes the version 4T instruction set. Architectural extensions were added for version 5TE to include DSP instructions, such as 16-bit signed MLA instructions, saturation arithmetic, etc. The ARM926EJ-S and ARM1026EJ-S cores are examples of Version 5 architectures. Version 6 added instructions for doing byte manipulations and graphics algorithms more efficiently. The ARM11 family implemented the Version 6 architecture. Version 7 architectures (which include the Cortex family of cores, such as the Cortex A8, Cortex M3 and Cortex R4) extended the functionality by adding things such as Thumb2, low-power features, and more security.

## Slide 258: 3.1 ARM’s CPU designs preceding the ARM Cortex family (7)
4.1 Single-core mobile processors (1)
Vendor | Family | Processor | CPU core | ISA | Year
ARM | ARMx (CPUs) |  | ARM1 Cortex-A5 | Armv1- Armv7 | 1985- 2009
Qualcomm | MSM MSM Snapdragon | MSM2 MSM3000 QSD8250 | Intel 80186 ARM7TDMI Scorpion | x86 (16-bit) Armv4 Armv7 | 1995 1998 2007
MediaTek | MTx | MT6218B | ARM7EjS | Armv3 | 2003
Intel | Atom | Many | Bonnel | x86 (64-bit) | 2008
Huawei | Kirin | K3V1 | ARM926EJ-S | Armv5 | 2009
Apple | -- Ax | S5L8900 A4 | ARM1176jzf-s Cortex-A8 | Armv6 Armv7 | 2007 2010
Samsung | -- Exynos | S3C44B0 3110 | ARM7TDMI Cortex-A8 | Armv4 Armv7 | 2000 2010
AMD | Cat | Many | Bobcat | x86 (64-bit) | 2011
Table: Emergence of single core mobile CPUs
How ARM became involved into implementing mobile processors?
The first mobile phones (aka cellphones), emerged in the beginning of the 2000’s.
Smartphones, were introduced in the second half of the 2000’, with devices
like RIM’s Blackberry 8100 (2006) or Apple’s iPhone (2007).
The mobile boom sparked the interest of many companies, so in the second half of
the 2000’s, a large number of vendors began designing mobiles while using mostly
ARM- or in-house designed Arm ISA-based cores, as indicated in the Table below.

## Slide 259: 3.1 ARM’s CPU designs preceding the ARM Cortex family (8)
The crucial point for ARM’s success in penetrating the mobile world is the lower power
consumption of ARM ISA-based designs, that mostly originates from the inherent
advantage of RISC type Arm ISAs vs. CISC type x86 ISAs in power consumption.
This difference arises from the fact that RISC architectures require less power for
decoding and operand fetching, since RISC processors decode fixed length instructions
and fetch operands basically from registers whereas CISC processors decode
variable length instructions and fetch operands both from registers and the memory.
Why could ARM break into the mobile world with their CPU designs?

## Slide 260: 3.1 ARM’s CPU designs preceding the ARM Cortex family (9)
CPU cores implementing the Armv3 – Armv6 ISA and their use in mobiles [29]

## Slide 261: 3.1 ARM’s CPU designs preceding the ARM Cortex family (10)
Evolution of the pipeline length of ARM v4 – Armv6 based CPU cores [30]
Armv4
Armv4
Armv5
Armv5
Armv6

## Slide 262: 3.1 ARM’s CPU designs preceding the ARM Cortex family (11)
Main features of the Armv5 – Armv6 based CPU cores (≈1999-2003) [31]

## Slide 263: 3.1 ARM’s CPU designs preceding the ARM Cortex family (12)
Introduction of multicore CPUs by ARM: the ARM11 MPCore (Armv6)
07/2003: First public disclosure of the ARM11 MPCore.
05/2004: ARM11 MPCore (multi core ARM11 with 1-4 cores) available for licensing
with an evaluation system for early software development.
It dynamically predicts the required performance and adjusts the voltage and
frequency accordingly.
The ARM11 MPCore incorporates the IEM (Intelligent Energy Manager).
It is basically a cache coherent symmetric multicore with up to 4 cores.

## Slide 264: 3.1 ARM’s CPU designs preceding the ARM Cortex family (13)
Block diagram of the ARM11 MPCore [32]
Note that the ARM11 MPCore does not include an L2.

## Slide 265
3.7 Case example: The core complex of the TCS22 platform
(Optional reading, not a part of the Lecture)

## Slide 266: 3.7 Case example: The core complex of the TCS22 platform (1)
3.7 Case example: The core complex of the TCS22 platform
Components of the Core Complex in the TCS22 platform -1 [81]
As shown above, the Core Complex of the TSC22 platform includes the Cortex-X3 big,
the Cortex-A715 middle cores, the Cortex-A510 little core module, and the related
DSU-110 DynamIQ Shared Unit, as depicted in the following Figure.

## Slide 267: 3.7 Case example: The core complex of the TCS22 platform (2)
The DynamIQ Core Complex, is part of a TCS22-based mobile SoC [82]
Next, we will outline the cores that may be part of the Core Complex of the
TCS22 platform, including the Cortec-X3, Cortex-A715 and Cortex-A510 cores.
Core Complex

## Slide 268: 3.7 Case example: The core complex of the TCS22 platform (3)
a) The high-performance Cortex-X3 core -1
It focuses on performance.
In contrast, the Cortex-A715 CPU prioritizes balanced performance and efficiency,
while the refreshed Cortex-A510 core module efficiency.
The Cortex-X3 is expected to be used predominantly in premium, large-screen
mobiles and laptops.

## Slide 269: 3.7 Case example: The core complex of the TCS22 platform (4)
instruction fetching,
instruction decoding,
branch prediction,
data prefetching,
instruction cache bandwidth,
MOP (Macro-Operation) cache,
OOO (Out-Of-Order) window size (ROB size)
Number of integer execution units.
From the enhancements enlisted above, subsequently, we want to address one
aspect, namely, the widening of the X3 core compared to the X1 core.
We will show how this change aligns with the evolution of the front-end width
of ARM cores from Armv8.2 to Armv9.0 –based cores).
The high-performance Cortex-X3 core -2
The new Armv9.0-A based cores do not provide mandatory support for the Aarch32 execution mode, except for the Cortex-A 710).
Consequently, the circuitry for implementing the AArch32 mode has been removed
in the Cortex-X2 core.
Subsequently, the new Cortex-X3 design has already been optimized for the
AArch64 mode.
The optimization covered most parts of the microarchitecture, including

## Slide 270: 3.7 Case example: The core complex of the TCS22 platform (5)
Widening the front-end width in Arm’s Cortex-A/X series cores [58]
In their high-performance cores, ARM increased the decode width first from 4 to 5
in the X1 core and then to 6 in the X3 core.
Additionally, ARM introduced MOP caches in the A77 core to improve the efficiency
of instruction decoding.
Their initial access width was increased from 6 to 8.
As a result, ARM was able to increase the dispatch rate of their cores from 4 to 6
and then from 6 to 8.
The impact of ARM’s continuous development is the substantial leap in the achieved
performance of their processors.

## Slide 271: 3.7 Case example: The core complex of the TCS22 platform (6)
Microarchitecture of the Cortex-X3 core [69]

## Slide 272: 3.7 Case example: The core complex of the TCS22 platform (7)
IPC uplift of Cortex-X3 cores compared to the previous Cortex-X2 cores [58]
As indicated in the Figure above, ARM achieved approximately a 10 % performance
boost in the SPECint_base2006 benchmark scores (measured on a set of real-world
applications, while calculating the geometric mean of the results).

## Slide 273: 3.7 Case example: The core complex of the TCS22 platform (8)
b) The balanced efficiency and performance Cortex-A715 big core
The Cortex-715 is the successor to the Cortex-A710, as indicated in the Figure below.
Figure: The sequence of ARM’s big and little cores [78]
ARMv8.2

## Slide 274: 3.7 Case example: The core complex of the TCS22 platform (9)
The Cortex-715 does not support the 32-bit AArch32 execution mode, unlike the
Cortex-710.
Consequently, all circuitry needed for the 32-bit mode could be removed,
simplifying the decoder design dramatically.
The Cortex-715 has a 5-wide decoder, an improvement over the previous 4-wide
decoder of the Cortex-A710, enabling a wider front end.
Additionally, it lacks an MOP cache, as depicted in the following Figure.
Key differences between ARM’s Cortex-A715 and Cortex-A710 cores

## Slide 275: 3.7 Case example: The core complex of the TCS22 platform (10)
Contrasting the front-ends of the Cortex-A715 and Cortex-A710 cores [78]

## Slide 276: 3.7 Case example: The core complex of the TCS22 platform (11)
Microarchitecture of the Cortex-A715 [69]

## Slide 277: 3.7 Case example: The core complex of the TCS22 platform (12)
Power-performance curves of the Cortex-A715 and A710 cores [78]
Obviously, the new design allows for higher performance at the same power
consumption or provides the same performance at a lower power consumption.

## Slide 278: 3.7 Case example: The core complex of the TCS22 platform (13)
ARM’s power/performance statements relating to their Cortex-A715 vs. the
Cortex-A710 cores [78]

## Slide 279: 3.7 Case example: The core complex of the TCS22 platform (14)
c) The high efficiency updated Cortex-A510 little core module
This is an updated version of the Armv9.0-A based Cortex-A510.
In big.little mobile designs, it is expected to be used as the little CPU.
In contrast to the 1. gen. Cortex-A510, the updated version optionally supports
the AArch32 ISA to allow its use in legacy mobile or IoT designs.
Unlike the Cortex-X2/X3 and Cortex-A710/715 CPUs the Cortex-A510/updated A510
is a dual core module, as mentioned and indicated in the next Figure.

## Slide 280: 3.7 Case example: The core complex of the TCS22 platform (15)
Example for substituting four “ordinary” little cores in an Armv8.2-A based
CPU by dual Armv9-A based A510 core modules [83]

## Slide 281: 3.7 Case example: The core complex of the TCS22 platform (16)
Cortex-A710
Architecture of the Cortex-A510/and updated A510 core modules [83]
ARM’s Cortex-A510/updated 510 core complexes consist of two Cortex-510 FX cores
with separate front-ends and scalar execution units.
Both cores share dual 64- or 128-bit wide NEON and SVE2 execution units and an
L2 cache, as indicated above.

## Slide 282: 3.7 Case example: The core complex of the TCS22 platform (17)
The fetch/decode/issue stages of the Cortex-A510/updated A510 core
modules -2 [84]
Both CPUs have a 3-wide in-order front-end, as seen above.

## Slide 283: 3.7 Case example: The core complex of the TCS22 platform (18)
Assumed microarchitecture of the Cortex-A510 core module [81]

## Slide 284: 3.7 Case example: The core complex of the TCS22 platform (19)
Example of an updated DSU-110 DynamIQ Shared Unit [85]
As indicated above, the DSU includes Armv9.0-based cores, the shared L3 cache,
and further units, not discussed here.
The max core count is 12.
The shared L3 cache is up to 16 MB sized.

## Slide 285
Annex 1: Cache-coherent interconnects

## Slide 286: Annex 1: Cache-coherent interconnects (1)
Caches are typically operated as write-back caches, meaning that data that has been
modified in the cache will not be immediately updated in the memory, instead
updating is deferred until the cache line needs to be evoked from the cache.
This method aims to reduce the memory traffic required for updating data.
However, in a multicore processor, when all cores share the same address space
and the cores include caches, read operations should always fetch the most
recent copy of the addressed data.
This requirement is referred to as cache coherency.
Cache coherency is governed by a cache coherency protocol that is followed while
reading or writing memory data.
On-die cache-coherent interconnects ensure cache coherency in recent shared
memory systems, such as in processors or multiprocessors.
Annex 1: Cache-coherent interconnects
First, let’s start by explaining what cache-coherency is.
Remark: Write-through caches, unlike write-back caches, write data into both the
cache and the memory simultaneously.

## Slide 287: Annex 1: Cache-coherent interconnects (2)
Principle of operation of on-die cache coherent interconnects (simplified) -1
Their kernel is a cache-coherent interconnection fabric.
It provides the interconnection between the linked components.
All the related processor components (or system components) are connected
to it through point-to-point links, as illustrated in the following Figure.
Interconnection fabric
(e.g. a crossbar
or a ring bus)
Point-to-point
links
Shared memory
Figure: Simplified schematics of a processor with an on-die cache coherent interconnect [63]

## Slide 288: Annex 1: Cache-coherent interconnects (3)
Principle of operation of on-die cache coherent interconnects (simplified) -2
Data is typically packetized, and data packets are sent from senders to receivers
through the interconnecting fabric.
Data transfers (reads and writes) are governed by a coherency protocol.
Typically, the cache-coherent interconnect includes a snoop filter to track the
locations of the most recent copies of memory data, reducing coherency traffic
and speeding up data fetches.
Cache-coherent interconnects have layered protocols (which will be shown later
but will not be further discussed).

## Slide 289: Annex 1: Cache-coherent interconnects (4)
Designation | Name | Vendor | Fabric | Year of intro. | First implemented in
HyperTransport | HT | AMD | crossbar | 2003 | K8-based Athlon64 (mobile) Opteron (servers)
Quick Path Interconnect | QPI | Intel | crossbar | 2008 | Core Nehalem (desktops/servers)
Quick Path Interconnect | QPI 1.1 | Intel | ring bus | 2010 | Core Sandy Bridge (desktops/servers)
AMBA Coherency Extension | ACE | ARM | crossbar | 2011 | Armv7 CPUs (mobiles), CCI-400?
Coherent Hub Interface | CHI | ARM | ring bus | 2014 | Arm8.0 CPUs (mobiles), CCI-500
Coherent Hub Interface | CHI Issue B | ARM | mesh | 2017 | Armv8.2 CPUs, CMN-600
Coherent Hub Interface | CHI Issue E | ARM | mesh | 2021 | Armv9 CPUs, NI-700
Ultra Path Interconnect | UPI | Intel | mesh | 2017 | Skylake-SP (servers)
Infinity | IF | AMD | crossbar | 2017 | Zen family 1. gen. (mobiles to servers)
Overview of cache-coherent interconnects -1

## Slide 290: Annex 1: Cache-coherent interconnects (5)
In order to provide insight into cache-coherent interconnects, we will now discuss
a few details of Intel’s widely used QPI interconnect.
Overview of cache-coherent interconnects -2

## Slide 291: Annex 1: Cache-coherent interconnects (6)
Interconnection fabric
(e.g. a crossbar
or a ring bus)
Quick Path Interconnects
Example: Simplified schematics of Intel’s cache coherent QPI interconnect [63]
Shared memory

## Slide 292: Annex 1: Cache-coherent interconnects (7)
Architectural layers of Intel’s QuickPath interconnect [63]
As depicted on the right,
the QPI has a layered architecture,
comprising of five layers
(only the Physical layer is detailed).

## Slide 293
The physical layer of the QPI interconnect [64]
Annex 1: Cache-coherent interconnects (8)
TX Unidirectional link
RX Unidirectional link
(Lane: Vonalpár)
It defines two unidirectional links; the TX Transmitter) and the Rx (Receiver) links.
Each link has 16 data lanes, 2 protocols, 2 CRC, and 2 clock lanes.
The lanes carry differential signals, as shown in the following Figure.
(Cyclic Redunndancy Code lanes.

## Slide 294
Principle of implementing differential signals [65]
Annex 1: Cache-coherent interconnects (9)
*

## Slide 295
LVDS: Low Voltage Differential Signaling LVTTL: Low Voltage TTL
(D)RSL: (Differential) Rambus Signaling Level SSTL: Stub Series Terminated Logic VCM: Common Mode Voltage VREF: Reference Voltage
LVTTL (3.3 V)
FPM/EDO
SDRAM
HI 1.5
TTL (5 V)
FPM/EDO
SSTL
SSTL2 (DDR)
SSTL1.8 (DDR2)
SSTL1.5 (DDR3)
RSL (RDRAM)
FSB
LVDS
PCIe
QPI, DMI, ESI
FB-DIMMs
Smaller voltage swings
DRSL
XDR (data)
Signaling systems used in buses
Annex 1: Cache-coherent interconnects (10)
Signals
Voltage referenced
Single ended
Differential
t
t
VREF
t
S+
S-
VCM
Typ.voltage
swings
600-800 mV
200-300 mV
3.3-5 V
Signaling
system
used in

## Slide 296
Example of a crossbar-based1 cache coherent interconnect implemented
in AMD’s Zen-based Ryzen APU lines (2017) [66].
Annex 1: Cache-coherent interconnects (11)
We note that AMD’s crossbar is not a full crossbar but a sparsely connected crossbar, as will be
discussed later in this Section.

## Slide 297: Annex 1: Cache-coherent interconnects (12)
Example of a ring bus-based cache-coherent interconnect of Intel’s 13th gen.
Raptor Lake processors featuring a big.little architecture with 8 big and 16 little
cores (2022) [67]

## Slide 298: Annex 1: Cache-coherent interconnects (13)
Example of a mesh-based cache-coherent interconnect implemented in Intel’s
32-core Skylake server processor (2017) [68]

## Slide 299: Annex 1: Cache-coherent interconnects (14)
2) The evolution of interconnect fabrics
This Subsection focuses on the kernel part of on-die interconnects, which is
the interconnect fabrics.
However, before discussing ARM’s latest cache coherent interconnect fabrics
, the CoreLink CI-700, it is compelling to trace their fascinating evolution.

## Slide 300: Annex 1: Cache-coherent interconnects (15)
Early off-die interconnects
Early client computers (desktops and laptops) were built on mainboards, with
system components interconnected through the chipset, including the north and
south bridges.
CPU
NB
SB
Per./IO
GPU
Per./IO
M
Per./IO
These implementations are designated as off-die processor interconnects.
The next two Figures illustrate the block diagram and an example layout of an
off-die processor interconnect.
Figure: Schematic view of an early
off-die processor interconnect

## Slide 301: Annex 1: Cache-coherent interconnects (16)
Example of an off-die processor interconnect: The Core 2 system architecture [69]

## Slide 302: Annex 1: Cache-coherent interconnects (17)
Evolution to SoCs (System on Chip) by implementing on-die interconnects
Over time, there has been an incredible evolution in system design, with more and
more processor components being integrated into the processor die.
These components include, for instance, the memory controller, the GPU, and the
IO (PCIe) control.
The culmination of this evolution was when the entire system became integrated
into the processor die, with an on-die processor interconnect linking all system
components together, like AMD’s Infinity Fabric (IF) or Intel’s Ring bus.
This type of system implementation, where all processor components are
integrated into the die, is referred to as System on Chip (SoC).
An example is depicted in the following diagram.

## Slide 303: Annex 1: Cache-coherent interconnects (18)
Ring bus-based
interconnect fabrics
Mesh-based
interconnect fabrics
Crossbar-based
interconnect fabrics
Main types of on-die interconnect fabrics used in processors
Main types of on-die processor interconnects used in client processors
Now, let's become acquainted with the basics of these interconnect fabrics!

## Slide 304: Annex 1: Cache-coherent interconnects (19)
Off-die processor interconnects
Processor interconnects
Used to interconnect
functional units of a processor off-die.
Used to interconnect
functional units of a processor on-die.
CPU
NB
SB
Per./IO
GPU
Per./IO
M
Per./IO
A: Accelerator (e.g. GPU)
MC: Memory Controller
a) Crossbar-based interconnect fabrics
Crossbar-based
interconnect fabrics
Crossbar
MC
IO
--
CPU
--
GPU
--
A crossbar-based fabric provides direct connections between all functional units,
as illustrated in the Figure on the right. .

## Slide 305: Annex 1: Cache-coherent interconnects (20)
(Crossbar)
Example of a crossbar-based interconnect fabric implemented in Intel’s Nehalem-
based DP-server processors (2008) [36]
Note: Nehalem-based desktop and
laptop processors employ
the same interconnect as
shown in the Figure
(but have no QPI links).

## Slide 306: Annex 1: Cache-coherent interconnects (21)
Example of a crossbar-based interconnect fabric introduced in AMD’s K10
Barcelona processors along with four-core core blocks (2008) [70]

## Slide 307
Example of a sparsely connected crossbar fabric of AMD’s Zen-based
1.gen. APU processors (2017) [66]
Annex 1: Cache-coherent interconnects (22)

## Slide 308: Annex 1: Cache-coherent interconnects (23)
Transfer from off-die interconnects to crossbar-based on-die interconnect fabrics
Crossbar-based
interconnect fabrics
Off-die
processor interconnects
Intel’s Core family-based multicores (2005-2010)
(up to and including) the Westmere processor line)
AMD’s Family K8-based multicores,
like the dual-core Athlon 64X2 (2005)
AMD’s quad-core Family K10 (Barcelona)-based lines (2007)
AMD’s Family 12h (Llano)-based lines (2011)
AMD’s Family 14h/16h) (Cat)-based lines (2011-2015)
AMD’s Family 15h (Bulldozer)-based lines (2011-2016)
AMD’s Family 17h (Zen-family)-based lines (from 2017 on)
Examples
Transfer from off-die interconnects to crossbar-based on-die interconnect fabrics
As stated above, AMD began using crossbar-based interconnect fabrics with its
K8 family and continued to use them until recently.
This is because AMD introduced quad-core core clusters along with its K10 Barcelona
line in 2007 as part of a strategic decision, and AMD’s crossbars manage
core clusters as single entities.
This greatly reduces the complexity of implementing crossbar interconnect fabrics.

## Slide 309: Annex 1: Cache-coherent interconnects (24)
Why did ring-bus-based processor interconnects emerge?
As the number of CPU cores increases, the complexity of crossbar switches also
raises rapidly.
This is because a crossbar which interconnects n components requires n x (n-1)
unidirectional links, while each link comprises a large number of lines
(say in the order of 100).
Therefore, for higher core counts (e.g., more than 6 CPU cores), implementing
crossbar switches as interconnection fabrics becomes too “costly.”
This is why ring buses emerged, replacing crossbar switches, as seen in the
next Figure.
b) Ring-bus-based interconnect fabrics

## Slide 310: Annex 1: Cache-coherent interconnects (25)
Switching from crossbar-based fabrics to ring bus-based ones for higher core counts
Crossbar-based
interconnect fabric
A: Accelerator (e.g. DSP, NPU)
MC: Memory Controller
Ring bus-based
interconnect fabric
Crossbar
MC
IO
--
CPU
--
GPU
--
Ring bus
MC
IO
--
CPU
--
A
GPU
--
--
Ring bus-based interconnect fabrics
Less costly implementation
for higher nc

## Slide 311: Annex 1: Cache-coherent interconnects (26)
Example: A few details of Intel’s ring bus-based interconnect fabric [71]
The ring-bus-based interconnect consists of four rings (to support cache coherency)
as follows:
two Data rings (running in opposite directions) carrying 32 bytes/clock cycle
one Request ring and one Snoop ring.
It is clocked at the core frequency.

## Slide 312: Annex 1: Cache-coherent interconnects (27)
Operation of Intel’s ring bus (as introduced in the Nehalem-EX server
processor in 2010) [72]
There are two counter-rotating rings.
The rings advance by one stop per cycle, transferring 32 bytes from stop to stop.
Senders inject data into empty slots.
Receivers take out data addressed to them.

## Slide 313: Annex 1: Cache-coherent interconnects (28)
2006
2008
2010
2012
2014
Year
IBM/Toshiba/Sony
Cell
(8C)
Graphics/HPC
Intel
Larrabee
(16C-24C)
Graphics/HPC)
Nehalem-EX
(8C)
Servers
Sandy Bridge
(4C+GPU
DT/mobiles
and all subsequent
server processors up to
Broadwell-based servers
Xeon Phi
Knights Ferry
(32C)
HPC
Xeon Phi
Knights Corner
(~60C)
HPC
ARM
CCN-504
(4 core clusters)
CCN-508
(8 core clusters)
CCN-502
CCN-512
(4/12 core clusters)
Emergence and use of on-die ring buses
and subsequent
DTs and mobiles
CCN: Cache-coherent Network

## Slide 314: Annex 1: Cache-coherent interconnects (29)
As the number of processor cores increases, ring bus-based solutions become less attractive due to the rising signal latency, as shown in the following Figure.
Why did mesh-based interconnect fabrics emerge? [72] -1
c) Mesh-based interconnect fabrics

## Slide 315: Annex 1: Cache-coherent interconnects (30)
Example: Long delays arising in a ring-based interconnect fabric (in Intel’s
Haswell-EX server processor, (2015) [73]

## Slide 316: Annex 1: Cache-coherent interconnects (31)
Therefore, for higher core counts a new interconnect fabric layout is needed.
The new design is the mesh interconnect, as will be discussed subsequently.
Why did mesh-based interconnect fabrics emerge? -2

## Slide 317: Annex 1: Cache-coherent interconnects (32)
Swithching from ring bus based interconnects to mesh based ones (e.g. servers)
Ring bus-based
interconnects
Mesh-based
interconnect
(for servers)
CoreLink CI-700 for clients
(CC, on CHI, 2021)
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
CC
CC
CC
CC
A
A
CC
CC
A
MC
MC
MC
MC
R
R
R
R
R
A
A
A
MC
MC
IO
IO
IO
IO
IO
IO
P
P
P
P
P
P
*
CC: Core Cluster
A: Accelerator (e.g. GPU, NPU)
nc: Core count
CCN-5xx interconnect for servers
(CC, on CHI, 2012)
Examples
Intel
ARM
Skylake-SP for servers
(CC, UPI, 2017)
Knights Landing for AI, (2016)
Sandy Bridge (CC, on QPI, 2011)
and subsequent processors
Less cost
for higher nc
Shorter
access time
for higher nc
Ring bus
MC
IO
--
CPU
--
A
GPU
--
--
Emergence of mesh-based interconnect fabrics in client processors

## Slide 318: Annex 1: Cache-coherent interconnects (33)
DMA, GPU
(IO peripherals)
(Accelerators
DMA devices)
The CoreLink CI-700 Cache-coherent Interconnect fabric (2021) [74] -2
It interconnects
1-8 DSU clusters
1-8 memory interfaces
3-24 accelerators and
DMA-devices and
1-4 IO peripherals.
It includes
1-8 System-Level Cache slices
of up to 4MB/slice
1-8 Snoop Filter slices
of up to 8 MB/slice
Note that a large Snoop Filter speeds up the process of ensuring cache coherency.
The Snoop Filter tracks the locations of the most recent memory data.

## Slide 319: Annex 1: Cache-coherent interconnects (34)
Example of a 2D mesh-based
interconnect fabric of ARM’s
CI-700 Cache-coherent interconnect [74]
The 2D mesh is configurable
up to the size: 4x3, as depicted
in the Figure on the right.
XPs (crosspoints) represent routers
that forward data packages.
Each router has two ports for
connecting processor components.

## Slide 320: Annex 1: Cache-coherent interconnects (35)
Why have dual interconnects become prevalent in processors?
When a processor (or computer system) includes functional units with caches,
like CPU cores or accelerators, and these functional units share the same
memory space, memory operations (reads and writes) have to maintain cache
coherency to always access the most recent copy of the referenced data.
This is achieved through using cache-coherent interconnects.
On the other hand, other functional units, like displays or IO controllers, do not
include caches and, therefore, do not require memory synchronization.
It follows that functional units without caches can be connected to the processor
or the system through a less complex interconnect.
Therefore, system design can be optimized by using two interconnects - one
cache-coherent and another non-cache-coherent – to link system components.
The following two Figures provide examples of this design approach.
3) Use of dual interconnects in processors

## Slide 321
Example 1: Use of dual interconnects in processors:
Intel’s Atom processor-based SoC architecture, revealed at IDF 2010 [75]
Annex 1: Cache-coherent interconnects (36)
The “low-power memory interconnect fabric” is presumably a ring bus.
There is no information about how the non-cache coherent IO fabric is implemented.
Cache coherent
fabric
Non-cache coherent
fabric

## Slide 322: Annex 1: Cache-coherent interconnects (37)
Example 2: Use of dual interconnects in processors:
Intel’s 11th gen. Tiger Lake processor (2020) [76]
The “Coherent fabric” is likely a ring bus.
There is no information about how the non-cache coherent fabric has been
implemented.

## Slide 323: Annex 1: Cache-coherent interconnects (38)
The use of Networks on a Chips (NoC) as non-cache-coherent interconnects
The NoC technology is based on routers, known as crosspoints, interconnected
according to a selected irregular pattern.
It’s important to note that the interconnection pattern is irregular and could be
seen as a sparse crossbar rather than as a 2D mesh.
Data is packetized, and data packets (also called flits) are forwarded from the
sender via the routers to the receiver.
An example of such a NoC is ARM’s CoreLink NI-700 non-cache coherent
interconnect, illustrated in the following Figure.

## Slide 324: Annex 1: Cache-coherent interconnects (39)
IO
Accelerators
Network
interface
modules
The Armv9-based CoreLink NI-700 non-cache-coherent NoC (2021) [74]
The processor components are connected to the NoC via Network interface modules,
marked by brick red colored rectangles.
These modules transform data sent by the processor components into fixed-length
data packets, which are then forwarded via the routers to the addressed receivers.