## Slide 1
Dezső Sima
April 2016
(Ver. 1.5)
 Sima Dezső, 2016
Intel’s High Performance
MP Servers and Platforms

## Slide 2
Intel’s high performance MP platforms
1. Introduction to Intel’ s high performance
multicore MP servers and platforms
2. Evolution of Intel’s high performance
multicore MP server platforms
5. References
3. Example 1: The Brickland platform
4. Example 2: The Purley platform
Notes: 2

## Slide 3: Intel’s high performance MP platforms
Remark
The material presented in these slides is restricted to Intel’s multicore MP servers and platforms.
They emerged as dual core MP servers based on the 3. core of the Pentium 4 (termed Prescott)
(called Paxville Xeon-MP or Xeon 7000 servers) about 2005.
Accordingly, previous systems are not covered.

## Slide 4
Introduction to Intel’s high performance
MP servers and platforms
1.1 The worldwide 4S (4 Socket) server market
1.2 The platform concept
1.3 Classification of server platforms
1.4 Naming scheme of Intel’s servers
1.5 Overview of Intel’s high performance multicore
MP servers and platforms
Notes: 4

## Slide 5
1.1 The worldwide 4S (4 Socket) server market
Notes: 5

## Slide 6: 1.1 The worldwide 4S (4 Socket) server market (1)
1. Introduction to Intel’s high performance multicore MP servers and platforms
1.1 The worldwide 4S (4 Socket) server market [52]

## Slide 7
1.2 The platform concept
Notes: 7

## Slide 8: 1.2 The platform concept (1)
1.2 The platform concept
The notion platform is widely used in different segments of the IT industry e.g. by
IC manufacturers, system providers or even by software suppliers with different interpretations.
Here we are focusing on the platform concept as used by system providers, like Intel or AMD.
The platform consists of three main components of the system architecture, being typically
The platform concept of system providers
The designation platform is often understood as the backbone of the system architecture.
the processor or processors (in multiprocessors)
the related chipset as well as
the interfaces (buses) interconnecting them.

## Slide 9: 1.2 The platform concept (2)
Core 2 (2C)
7200
631xESB/ 632xESB IOH
FSB
Core 2 (2C)
FB-DIMM
w/DDR2-533
ESI
1066 MT/s
Example 1: A simple traditional DC DP (2S) server platform (2007)

## Slide 10: 1.2 The platform concept (3)
Example 2: A recent 4S platform
(The Brickland 4S server platform including Haswell-EX processors (2015)
ME: Management Engine
QPI 1.1: Up to 9.6 GT/s
QPI
1.1
QPI
1.1
QPI 1.1
QPI 1.1
QPI 1.1
QPI 1.1
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI2
channels
2x4 SMI2
channels
Xeon E7-4800 v3
(Haswell-EX)
Haswell-EX 14C
Haswell--EX 14C
Haswell-EX 14C
Haswell-EX 14C
SMI2: Scalable Memory Interface 2
(Parallel 64-bit VMSE data link between
the processor and the SMB)
SMB: Scalable Memory Buffer
(C112/C114: Jordan Creek 2)
(Performs conversion between the
parallel SMI2 and the parallel
DDR3/DDR4 DIMM interfaces)
C112: 2 DIMMs/channel
C114: 3 DIMMs/channel
Up to DDR3-1600
in both performance and lockstep modes and
up to DDR4-1866 in lockstep mode
PCIe 3.0
32
PCIe 3.0
32
C602J PCH
(Patsburg J)
DMI2
4xPCIe2
ME
PCIe 3.0
32
PCIe 3.0
32
SMB

## Slide 11: 1.2 The platform concept (4)
Compatibility of platform components (2)
Due to the fact that the platform components are connected via specified interfaces
multiple generations of platform components, such as processors or chipsets of a given line
are often compatible as long as they make use of the same interfaces and interface parameters
(such FSB speed) do not restrict this.

## Slide 12: 1.2 The platform concept (5)
Nehalem-EX 8C
Westmere-EX 10C
7500 IOH
QPI
QPI
QPI
QPI
QPI
QPI
QPI
QPI
SMB
SMB
Nehalem-EX: up to DDR3-1067
Westmere-EX: up to DDR3-1333
SMB
SMB
SMB
SMB
SMB
SMB
ICH10
ESI
SMI: Scalable Memory Interface
(Serial link between the processor
and the SMB)
SMB: Scalable Memory Buffer
(Performs conversion between the
serial SMI and the parallel
DDR3 DIMM interfaces)
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI
channels
2x4 SMI
channels
Example for compatibility of platform components
(The Boxboro-EX platform 2010/2011)
ME
ME: Management Engine
Xeon 7500
(Nehalem-EX)
(Becton) 8C
Xeon E7-4800
(Westmere-EX) 10C
Nehalem-EX 8C
Westmere-EX 10C
Nehalem-EX 8C
Westmere-EX 10C
Nehalem-EX 8C
Westmere-EX 10C
/
Figure: The Boxboro-EX MP server platform supporting Nehalem-EX/Westmer-EX server processor
2 DIMMs/memory channel
4 x QPI up to 6.4 GT/s
36
PCIe
2.0

## Slide 13
1.3 Classification of server platforms
Notes: 13

## Slide 14
1.3.1 Overview
Notes: 14

## Slide 15: 1.3.1 Overview (1)
1.3.1 Overview
Server platforms my be classified according to three main aspects, as follows:
according to the number of processors supported (Section 1.3.2)
according to their memory architecture (Section 1.3.3)
according to the number of chips constituting the chipset (Section 1.3.3)

## Slide 16
1.3.2 Server platforms classified according to the number of
processors supported
Notes: 16

## Slide 17: 1.3.2 Server platforms classified according to the number of processors supported (1)
1.3.2 Server platforms classified according to the number of processors supported
DP (2S)
server platforms
Server platforms classified
according to the number of processors supported
Platforms for more than four servers
2- processor server platforms
(2-socket server platforms)
MP (4S)
server platforms
4-processor server platforms
(4-socket server platforms)
(Server platforms for
more than four sockets)
Uniprocessor server platforms
(UP-server platforms)
1-processor server platforms
(1-socket server platforms)
Multiprocessor server platforms
Server platforms supporting more than one processor
(Multi-socket server platforms)

## Slide 18
1.3.3 Server platforms classified according to
their memory architecture
Notes: 18

## Slide 19: 1.3.3 Server platforms classified according to their memory arch. (1)
1.3.3 Server platforms classified according to their memory architecture (1)
SMPs
(Symmetrical MultiProcessor)
Server platforms classified
according to their memory architecture
NUMAs
Multiprocessors (Multi socket system)
with Non-Uniform Memory Access
Multiprocessors (Multi socket system)
with Uniform Memory Access (UMA)
Typical examples
Processor
MCH
ICH
FSB
Processor
E.g. DDR2-533
ESI
All processors access main memory by the same
mechanism, (e.g. by individual FSBs and an MCH).
A particular part of the main memory can be accessed
by each processor locally, other parts remotely.
E.g. DDR3-1333
Processor
IOH1
QPI
QPI
ICH
ESI
QPI
E.g. DDR3-1333
Processor
1ICH: I/O hub
ESI: Enterprise System Interface

## Slide 20: 1.3.3 Server platforms classified according to their memory arch. (2)
SMPs
(Symmetrical MultiProcessor)
NUMAs
All processors share the same memory space
and all processors access memory by
the same access mechanism,
(e.g. by the same FSB or by individual FSBs
and an MCH.
All processors share the same memory space, but
each processor is allocated a particular part of the
memory space, called the local memory space,
whereas the rest is considered as the remote
memory spaces.
Multiprocessor server platforms
classified according to their memory architecture
Main features of SMP-type and NUMA-type server platforms
Consequently, all processors access memory
basically with the same latency.
The local part of the main memory can be accessed
by each processor immediately, e.g. via their private
on-die memory controller,
whereas the remote parts of the main memory will be
accessed via the processor owing the requested
memory space.
Consequently, processors access their local memory
space in significantly shorter latency than
memory spaces remote to them.
Multiprocessors
with Non-Uniform Memory Access

## Slide 21: 1.3.3 Server platforms classified according to their memory arch. (3)
Example of measured read latencies of uncached data [73]
Read latencies depend on whether referenced data is kept in the own or remote main memory space.
a) Read latency when referenced data is kept in the own memory space
Read latency:
65.1 ns (190 cycles)

## Slide 22: 1.3.3 Server platforms classified according to their memory arch. (4)
b) Read latency when referenced data is kept in the remote memory space [73]
Read latency:
106 ns (~310 cycles)
Read latency is increased now by the inter-processor access penalty of 41 ns in this case.

## Slide 23
1.3.4 Server platforms classified
according to the number of chips constituting the chipset
Notes: 23

## Slide 24: 1.3.4 Platforms classified according to the number of chips constituting the chipset (1)
Three-chip implementation
Server platforms classified
according to the number of chips constituting the chipset
Two-chip implementation
The system architecture consists
basically of three chip types
(processors/MCH/ICH)
The system architecture consists
basically of two chip types
(processors/PCH)
1.3.4 Server platforms classified according to the number of chips constituting
the chipset
Truland platform (2005/2006)
Caneland platform (2007/2008)
Boxboro-EX platform (2010/2011)
Brickland platform (2014/2015)
Purley platform (2017?)
SoC implementation
The system architecture consists
basically of a signle in-package SoC
(incorporating two chips)
Yet unknown platform with
Intel's Xeon D processor (2015)

## Slide 25: 1.3.4 Platforms classified according to the number of chips constituting the chipset (2)
Nehalem-EX 8C
Westmere-EX 10C
7500 IOH
QPI
QPI
QPI
QPI
QPI
QPI
QPI
QPI
SMB
SMB
Nehalem-EX: up to DDR3-1067
Westmere-EX: up to DDR3-1333
SMB
SMB
SMB
SMB
SMB
SMB
ICH10
ESI
SMI: Scalable Memory Interface
(Serial link between the processor
and the SMB)
SMB: Scalable Memory Buffer
(Performs conversion between the
serial SMI and the parallel
DDR3 DIMM interfaces)
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI
channels
2x4 SMI
channels
Example of a 3-chip platform: The Boxboro-EX 4S server platform supporting
Nehalem-EX/Westmere-EX processors (2010/2011)
ME
ME: Management Engine
Xeon 7500
(Nehalem-EX)
(Becton) 8C
Xeon E7-4800
(Westmere-EX) 10C
Nehalem-EX 8C
Westmere-EX 10C
Nehalem-EX 8C
Westmere-EX 10C
Nehalem-EX 8C
Westmere-EX 10C
/
Nehalem-EX aimed Boxboro-EX MP server platform (for up to 10 C)
2 DIMMs/memory channel
4 x QPI up to 6.4 GT/s
36
PCIe
2.0

## Slide 26: 1.3.4 Platforms classified according to the number of chips constituting the chipset (3)
Example of a 2-chip platform: The Brickland-EX 4S server platform supporting
Ivy Bridge-EX/Haswell-EX processors
ME: Management Engine
QPI 1.1: Up to 9.6 GT/s
QPI
1.1
QPI
1.1
QPI 1.1
QPI 1.1
QPI 1.1
QPI 1.1
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI2
channels
2x4 SMI2
channels
Xeon E7-4800 v3
(Haswell-EX)
Haswell-EX 18C
Haswell--EX 18C
Haswell-EX 18C
Haswell-EX 18C
SMI2: Scalable Memory Interface 2
(Parallel 64-bit VMSE data link between
the processor and the SMB)
SMB: Scalable Memory Buffer
(C112/C114: Jordan Creek 2)
(Performs conversion between the
parallel SMI2 and the parallel
DDR3/DDR4 DIMM interfaces)
C112: 2 DIMMs/channel
C114: 3 DIMMs/channel
Up to DDR3-1600
in both performance and lockstep modes and
up to DDR4-1866 in lockstep mode
PCIe 3.0
32
PCIe 3.0
32
C602J PCH
(Patsburg J)
DMI2
4xPCIe2
ME
PCIe 3.0
32
PCIe 3.0
32
SMB

## Slide 27: 1.3.4 Platforms classified according to the number of chips constituting the chipset (4)
Example of a Xeon D processor based (two chip) SoC server from Intel (2015) [130]
BMC: Baseboard Management Controller

## Slide 28: 1.3.4 Platforms classified according to the number of chips constituting the chipset (5)
Block diagram of Intel's Broadwell-based Xeon D server processor [130]

## Slide 29
1.4 Naming schemes of Intel’s servers
Notes: 29

## Slide 30: 1.4 Naming scheme of Intel’s servers (1)
1.4 Naming schemes of Intel’s servers
In 2005 Intel discontinued their previous naming scheme emphasizing clock frequency
like Xeon 2.8 GHz DP or Xeon 2.0 GHz MP, and introduced an AMD like naming scheme,
as follows:
9000 series
Intel’s recent naming scheme of servers
3000 series
5000 series
UP server
processor lines
Itanium lines
of processors
7000 series
MP server
processor lines
DP server
processor lines
Accordingly, Intel’s subsequent MP server processor lines were designated as follows:
Line | Processor | Based on
7000 | Paxville MP | Pentium 4 Prescott MP
7100 | Tulsa | Pentium 4 Prescott MP
7200 | Tigerton DC | Core 2
7300 | Tigerton QC | Core 2
7400 | Dunnington | Penryn
7500 | Beckton | Nehalem

## Slide 31: 1.4 Naming scheme of Intel’s servers (2)
Product line: E7, E5 or E3.
Wayness: How many processors are natively supported in a system
Westmere (without version number)
v2: Ivy Bridge
v3: Haswell
v4: Broadwell
Renewed naming scheme of Intel’s servers
In 4/2011 Intel renewed their naming scheme for their whole processor offering.
This results in the following new naming scheme for servers:
e.g. 8: high performance
6: effective performance etc..
Version: Xeon processors with a common version number share a common microarchitecture
Figure: Intel’s new Xeon naming scheme [127]
SKU (Stock Keeping Unit): Model number
Socket type: Signifies processor capability,

## Slide 32: 1.4 Naming scheme of Intel’s servers (3)
Haswell
(LGA1150)
Mobiles and desktops
Up to 4 cores
i3/i5/i7 designations
Haswell-E
(LGA2011)
High end desktops (HED)
Up to 8 cores
i7 designation
The Haswell family
Haswell-EP
(LGA2011)
Effective performance servers
Up to 18 cores
Haswell-EX
(LG2011)
High-end performance servers
Up to 18 cores
Example: Product lines of the Haswell family

## Slide 33: 1.4 Naming scheme of Intel’s servers (4)
Haswell
(LGA1150)
Mobiles and
desktops
Up to 4 cores
i3/i5/i7 designations
Haswell-E
(LGA2011)
High end desktops
(HED)
Up to 8 cores
i7 designation
The Haswell family
Haswell-EP
(LGA2011)
Effective perf.
servers
Up to 18 cores
Haswell-EX
(LG2011)
High-end
servers
Up to 18 cores
Servers
E3-1220L v3, 2C, 5/2014
E3-12x4L/12x5L/12x6L v3, 4C+G, 6/2013. 2/2014 and 5/2014
E3-1230L/1240L v3, 4C, 6/2013 and 5/2014
UP Servers
E3-12x5/12x6 v3, 4C+G, 6/2013 and 5/2014
E3-12x0/12x1 v3, 4C, 6/2013 and 5/2014
E5-16xx v3, 4/6/8/10/12/14C, 9/2014
Workstations/
microservers
DP-Servers
MP-Servers
E5-26xx v3, 4/6/8/10/12/14/16/18C, 9/2014
E5-46xx v3, 6/10/12/14/16/18C, 6/2015
E7-48xx v3, 8/10/12/14, 5/2015
E7-88xx v3, 4/10/16/18C, 5/2015
Example: Product lines of the Haswell family
Haswell-EN
(LGA1356-3)
Entry level
servers
Up to 10 cores
E5-24xxL v3, 4/6/8/10C, 1/2015
E5-14xxL v3, 8C, 1/2015
Haswell-WS
(LGA1150)
Workstations/
microservers
Up to 10 cores

## Slide 34: 1.4 Naming scheme of Intel’s servers (5)
Accordingly, beginning with the Westmere-EX line Intel’s high-end 4S server lines are
designated as follows:
E7-4800 (Westmere-EX line)
E7-4800 v2 (Ivy Bridge-EX line)
E7-4800 v3 (Haswell-EX line)
E7-4800 v4 (Broadwell-EX line)
Resulting naming of Intel’s high-end MP (4S) servers

## Slide 35: 1.4 Naming scheme of Intel’s servers (6)
Remark
The designation of the server generations v2, v3 etc. does not coincides with the designation
of the microarchitectures, as follows:
Microarchitecture | Architecture generation | Server generation
Westmere |  | (without designation)
Sandy Bridge | Gen. 2 | 
Ivy Bridge | Gen. 3 | v2
Haswell | Gen. 4 | v3
Broadwell | Gen. 5 | v4
Skylake | Gen. 6 | 

## Slide 36
1.5 Overview of Intel’s high performance multicore MP servers
and platforms
Notes: 36

## Slide 37: 1.5 Overview of Intel’s high performance multicore MP servers and platforms (1)
1.5 Overview of Intel’s high performance multicore MP servers and platforms -1
Truland
(2005)
(90/65 nm)
Intel’s high performance multicore MP server platforms
Brickland-EX
(2014)
(22 nm)
Boxboro-EX
(2010)
(45/32 nm)
Caneland
(2007)
(65/45 nm)
Purley
(2017?)
(14 nm)
Pentium 4 Xeon MP
based
Ivy Bridge-EX/
Haswell-EX
Broadwell-EX
based
Nehalem-EX/
Westmere-EX
based
Core 2 Xeon MP
based
Skylake-EX
based

## Slide 38
 | Core | Techn. | Intro. | High performance MP server processor lines | Core count | Chipset | Proc. socket
Truland MP | Pentium 4 MP Prescott | 90 nm | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 1C | E8500 + ICH5 | LGA 604
 | Pentium 4 Presc. | 90 nm | 11/2005 | 7000 (Paxville MP) | 2x1C | E8501 + ICH5 | 
 | Pentium 4 Presc. | 65 nm | 8/2006 | 7100 (Tulsa) | 2x1C |  | 
Caneland MP | Core2 | 65 nm | 9/2007 | 7200 (Tigerton DC) 7300 (Tigerton QC) | 2C 2x2C | E7300 (Clarksboro)+ 631x/632x ESB | LGA 604
 | Penryn | 45 nm | 9/2008 | 7400 (Dunnington) | 6C |  | 
Boxboro-EX | Nehalem | 45 nm | 3/2010 | 7500 (Beckton/ Nehalem-EX) | 8C | 7500 (Boxboro) + ICH10 | LGA 1567
 | Westmere | 32 nm | 4/2011 | E7-4800 (Westmere-EX) | 10C |  | 
 | Sandy Bidge | 32 nm |  |  |  |  | 
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-4800 v2 (Ivy Bridge-EX) | 15C | C602J (Patsburg J) | LGA 2011-1
 | Haswell | 22 nm | 5/2015 | E7-4800 v3 (Haswell-EX) | 14C |  | 
 | Broadwell | 14 nm | Q2/2016 | E7-4800 v4 (Broadwell-EX) | 24C |  | 
Purley | Skylake | 14 nm | 2017?? | n.a. (Skylake-EX) | 28C | Lewisburg | Socket P
Overview of Intel’s high performance multicore MP servers and platforms -2
1.5 Overview of Intel’s high performance multicore MP servers and platforms (2)

## Slide 39: 1.5 Overview of Intel’s high performance multicore MP servers and platforms (3)
Remark: Intel’s transfer to 64-bit ISA in their server lines [97]

## Slide 40
2. Evolution of Intel’s high performance
multicore MP server platforms
Notes: 40

## Slide 41
 | Core | Techn. | Intro. | High performance MP server processor lines | Core count | Chipset | Proc. socket
Truland MP | Pentium 4 MP Prescott | 90 nm | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 1C | E8500 + ICH5 | LGA 604
 | Pentium 4 Presc. | 90 nm | 11/2005 | 7000 (Paxville MP) | 2x1C | E8501 + ICH5 | 
 | Pentium 4 Presc. | 65 nm | 8/2006 | 7100 (Tulsa) | 2x1C |  | 
Caneland | Core2 | 65 nm | 9/2007 | 7200 (Tigerton DC) 7300 (Tigerton QC) | 2C 2x2C | E7300 (Clarksboro)+ 631x/632x ESB | LGA 604
 | Penryn | 45 nm | 9/2008 | 7400 (Dunnington) | 6C |  | 
Boxboro-EX | Nehalem | 45 nm | 3/2010 | 7500 (Beckton/ Nehalem-EX) | 8C | 7500 + ICH10 | LGA 1567
 | Westmere | 32 nm | 4/2011 | E7-4800 (Westmere-EX) | 10C |  | 
 | Sandy Bidge | 32 nm |  |  |  |  | 
Brickland | Ivy Bridge | 22 nm | 11/2012 | E7-4800 v2 (Ivy Bridge-EX) | 15C | C602J (Patsburg J) | LGA 2011-1
 | Haswell | 22 nm | 5/2015 | E7-4800 v3 (Haswell-EX) | 14C |  | 
 | Broadwell | 14 nm | Q2/2016 | E7-4800 v4 (Broadwell-EX) | 24C |  | 
Purley | Skylake | 14 nm | 2017?? | n.a. (Skylake-EX) | 28C | Lewisburg | Socket P
2. Evolution of Intel’s high performance multicore MP server platforms (1)
Intel’s high performance multicore MP (4S) platforms -- Overview
2. Evolution of Intel’s high performance multicore MP server platforms

## Slide 42: 2. Evolution of Intel’s high performance multicore MP server platforms (2)
In designing multiprocessor server platforms built up of multicore processors providing enough memory bandwidth is one of the key challenges.
It has three main reasons;
Their total memory bandwidth demand is directly proportional with the product of the processor count and the core count [99].
In MP processors core counts rise faster than memory speed, as the next Figures
will show.
The driving force of the evolution of memory subsystems in MP servers -1

## Slide 43: 2. Evolution of Intel’s high performance multicore MP server platforms (3)
Core count
2006
2008
2010
2012
2014
2016
Year
7000
(90 nm)
7300
(65 nm)
7400
(45 nm)
Nehalem-EX
(45 nm)
Westmere-EX
(32 nm)
Ivy-Bridge-EX
(22 nm)
Broadwell-EX
(14 nm)
*
*
*
*
*
2
4
8
16
32
24
10
6
15
*
*
(~2x/4 years)
(~2x/2 years)
Raising the core count in Intel’s MP platforms

## Slide 44: 2. Evolution of Intel’s high performance multicore MP server platforms (4)
Core count
2006
2008
2010
2012
2014
2016
Year
K8/800
Egypt
(90 nm)
K10/8300
Barcelona
(65 nm)
K10.5/8400
Istambul
(45 nm)
Bulldozer 6200
2xOrochi die
(32 nm)
Piledriver 6300
2xWarsaw die
*
*
*
*
*
2
4
8
16
32
24
10
6
15
*
*
(< 2x/2 years)
(~2x/2 years)
12
Piledriver 6300
2xAbu Dhabi die
(32 nm)
K10.5 6100
2xIstambul die
(45 nm)
?
Raising the core count in AMD's MP platforms

## Slide 45: 2. Evolution of Intel’s high performance multicore MP server platforms (5)
By contrast memory speed doubled at the beginning of the multicore era in about
every four years, and after DDR3 memory technology was arrived, only in about eight
years, as indicated in the next Figure.
The driving force of the evolution of memory subsystems in MP servers -2
As the Figures indicate core counts doubled in Intel's and AMD's MP servers
first in about every two years, in accordance with Moore’s revised law, but
beyond about 8 cores (or below about 45 nm) their growth rate has slowed down
to doubling in about 4 years, as demonstrated.

## Slide 46: 2. Evolution of Intel’s high performance multicore MP server platforms (6)
*
*
*
*
Transfer rate (MT/s)
100
500
Year
03
05
01
02
04
06
07
08
1000
3000
200
2000
~ 2*/4 years
DDR2
533
DDR2
667
DDR2 800
DDR3
1600
09
11
2010
12
13
15
DDR3
1067
2000

14
*
*
DDR3
1333
*
DDR4/2133
DDR3/1866
*
*
*
DDR
333
~ 2*/8 years
DDR
266
x
x
x
x
x
*
DDR
400
DDR2
667
DDR3
1600
DDR3
1866
DDR
400
DDR3
1067
DT
MP
Raising the memory transfer rate in Intel’s DT and MP platforms

## Slide 47: 2. Evolution of Intel’s high performance multicore MP server platforms (7)
It follows, that the required memory bandwidth which is directly proportional with the core count, and is given by the product of the number of memory channels, memory speed and data width, raises slower than needed.
Consequently, the bandwidth deficit need to be compensated by implementing appropriately more memory channels, if core count proportional memory bandwidth should be provided.
Here we assume that the width of the memory channels remains unchanged.
The driving force for the evolution of memory subsystems in MP servers -3
c) The number of feasible memory channels is however severely limited typically to two
when high speed memory (e.g. DDR2/3/4) is connected in the traditional way, that is
by parallel DRAM channels via the MCH.

## Slide 48: 2. Evolution of Intel’s high performance multicore MP server platforms (8)
Intel’s first generation MP servers made use of an SMP (Symmetric Multiprocessor) topology
while using only a single FSB that connects all 4 single core processors to the MCH
(North Bridge), and provided only two memory channels, as shown below.
Figure: Pentium 4 MP aimed MP server platform for single core processors
Xeon MP1
SC
Xeon MP1
SC
FSB
Xeon MP1
SC
Xeon MP1
SC
ICH
NB
E.g. HI 1.5
HI 1.5 266 MB/s
E.g. DDR-200/266
E.g. 400 MT/s
Example for a traditonal platform with only two memory channels
(Pentium 4-based single core Xeon MP platform)

## Slide 49: 2. Evolution of Intel’s high performance multicore MP server platforms (9)
If high speed (e.g. DDR2/3/4) DIMMs are connected via the MCH to a platform by standard
parallel memory buses, a large number of cupper traces are needed on the mainboard, e.g.
240 traces for DDR2/DDR3 DIMMs, to connect the MCH to the DIMM sockets, as shown in the
next Figure.
Why the number of memory channels is typically limited to two ? -1

## Slide 50: 2. Evolution of Intel’s high performance multicore MP server platforms (10)
All these DIMMs
are 8-byte wide.
Pin counts of SDRAM to
DDR4 DIMMs
SDRAM
(SDR)
DDR
DDR2
DDR3
168-pin
184-pin
240- pin
240-pin
DDR4
284-pin
2.1 Overview of the Truland MP platform (1)
Notes: 50

## Slide 51: 2. Evolution of Intel’s high performance multicore MP server platforms (11)
For implementing more than two memory channels smaller and denser cupper traces
would be required on the mainboard due to space limitations.
This however, would cause higher ohmic resistance and coupling capacitance, which
would end up in longer rise and fall times, i.e. it would prevent the platform from
maintaining the desired high DRAM rate.
The fact that basically no more than two high speed memory channels can be connected
directly to the MCH, limits the usability of connecting memory to the MCH by standard
memory channels more or less to single core MP servers, as shown in the next Figure.
Why the number of memory channels is typically limited to two? -2

## Slide 52: 2. Evolution of Intel’s high performance multicore MP server platforms (12)
Intel’s first generation MP servers made use of an SMP (Symmetric Multiprocessor) topology
while using only a single FSB that connects all 4 single core processors to the MCH
(North Bridge), and provided only two memory channels, as shown below.
Figure: Pentium 4 MP aimed MP server platform for single core processors
Xeon MP1
SC
Xeon MP1
SC
FSB
Xeon MP1
SC
Xeon MP1
SC
ICH
NB
E.g. HI 1.5
HI 1.5 266 MB/s
E.g. DDR-200/266
E.g. 400 MT/s
Example for a traditonal platform with only two memory channels
(Pentium 4-based single core Xeon MP platform)

## Slide 53: 2. Evolution of Intel’s high performance multicore MP server platforms (13)
Addressing the memory bandwidth bottleneck in MP servers built up of multicores
with more than two cores
The memory bandwidth bottleneck arising from attaching memory by standard DRAM channels
via the MCH can be remedied in two orthogonal ways, as indicated below.
Connect memory immediately
to the processor(s)
Use low line count interfaces
between the MC and the DIMMs
Possible solutions for raising the number of memory channels
DIMMs

## Slide 54: 2. Evolution of Intel’s high performance multicore MP server platforms (14)
Connect memory
via the MCH (Memory Control Hub)
Connection point of the memory
Connecting memory centrally
to the platform
causes severe bandwidth imitations
first of all for MP configurations.
Connect memory immediately to the processor
This is a further option of the design aspect of choosing the connection point of the memory
to the platform.
Connect memory
immediately to the processor(s)
Memory
Per processor connection of memory
provides inherent scaling with the processor count
of memory bandwidth with the processor count.
Memory
Processor
MCH
ICH
FSB
Processor
E.g. DDR2-533
ESI
E.g. DDR3-1333
E.g. DDR3-1333
ESI: Enterprise
System Interface
Processor
IOH1
QPI
QPI
ICH
ESI
QPI
Processor
1ICH: I/O hub
Memory

## Slide 55: 2. Evolution of Intel’s high performance multicore MP server platforms (15)
Layout of the interface connecting the MCs and the DIMMs
Connect DIMMs directly to the MCs
(via standard DRAM interfaces)
DIMMs are connected to one or more memory controllers directly by standard DRAM interfaces.
The number of memory channels is limited due to spatial and electrical constraints typically to two.
MC in
MCH/processor
Standard DRAM
interface
DIMMs
Use low line count interfaces between the MC and the DIMMs
This is a further option of the design aspect of choosing the interface between the MC and the
DIMMs.
Connect DIMMs via
memory extension buffers (MBs) with
low line count interfaces
to the memory controllers (MCs)
DIMMs are connected to one or more memory controllers via low line count interfaces and interface converters, called memory extension buffers (MBs) in order to connect more than two memory channels to the MCs
MB
MB
MC in
MCH/processor
Standard DRAM
interface
Low line count
interface
DIMMs

## Slide 56: 2. Evolution of Intel’s high performance multicore MP server platforms (16)
Connect DIMMs directly
to the MCs
(via standard DRAM interfaces)
Layout of the interface
connecting the MCs and the DIMMs
Use dedicated parallel
interfaces
between MCs and MBs
Use dedicated
serial interfaces
Connect DIMMs
via memory extension buffers (MBs) with
low line count interfaces
to the memory controllers (MCs)
Use standard
FB-DIMM interfaces
Intel's serial links (IMI/SMI)
have about 50-70
active signal lines
(vs. about 150 in
standard DRAMs)
Intel aims to reduce power
by using dedicated parallel links
(SMI2) between the MC(s)
and the MBs
Intel's dedicated parallel link
has about 110 signal lines
Truland MP platform
(2005/2006)
Caneland platform
(2007/2008)
Boxboro-EX platform
(2010/2011)
Brickland platform
(2014/2015)
Previous
MP platforms
FB-DIMM channel
have about 50
active signal lines
(vs. about 150 in
standard DRAMs)
Use serial (packetized)
interfaces
between MCs and MBs
Layout of the interface between the MCs and the DIMMs

## Slide 57: 2. Evolution of Intel’s high performance multicore MP server platforms (17)
Fig. 7
Connecting memory
to the MCH(s)
(SMPs)
Connection point
of the memory
Connecting memory
to the processor(s)
(NUMAs)
Intel
Caneland (2007/08)
2C/2x2C/6C
Intel
Brickland (2014/15)
15C/18C
ARM
(MCs are linked via the
CCN-5xx interconects
to the platform
2012-2014)
16C/32C/48C
Intel
Truland MP (2005/06)
1C/2x1C/2C
Intel
Boxboro EX (2010/11)
8C/10C
Previous MP
platforms
1C
Connect DIMMs
directly to the
memory controllers (MC)
Use standard FB-DIMM interfaces
Use dedicated serial (packetized) interfaces
Use serial (packetized) interfaces
between MCs and MBs
Use dedicated parallel interfaces between the MCs and the MBs
Layout of the interface connecting the MCs and the DIMMs
Connect DIMMs via memory extension buffers (MBs) with low line count interfaces
to the memory controllers (MC)

## Slide 58: 2. Evolution of Intel’s high performance multicore MP server platforms (18)
Assessing the number of memory channels required
As stated before, in MP servers the core count is raising more or less according to Moore’s
rule, i.e. it doubles about every two years, whereas memory speed raises slower,
it doubles only about every four to eight years.
If the arising bandwidth deficit should be compensated by raising the number of memory
channels, assuming otherwise unchanged platform conditions, like clock speed, width of
the memory channels etc.., a scaling rule can be formulated as follows:
nM ~ √2 x √nC.
It can be shown (related publication in preparation) that an up to date MP platform with
as many cores as feasible and using available high speed memory, will have linear memory
bandwidth scaling in respect to the core count (nC) if the number of memory channels
per socket (nM) amount to

## Slide 59: 2. Evolution of Intel’s high performance multicore MP server platforms (19)
Expected number of memory channels (nM/socket) for different core counts (nC)
arising from the scaling rule of memory channels

## Slide 60: 2. Evolution of Intel’s high performance multicore MP server platforms (20)
The FSB bottleneck in SMP configurations
In early SMP configurations (e.g. in first Pentium 4 based single core (SC) Xeon based systems)
there is a single FSB that interconnects the four processors with the NB (Northbridge),
as seen.
Xeon MP1
SC
Xeon MP1
SC
FSB
Xeon MP1
SC
Xeon MP1
SC
ICH
NB
E.g. HI 1.5
HI 1.5 266 MB/s
E.g. DDR-200/266
Figure: Pentium 4 MP aimed MP server platform (for single core processors)
E.g. 400 MT/s
As the bandwidth data on the Figure demonstrate, in the example there is already the FSB
that limits the overall memory bandwidth.
Up to 3.2 GB/s
Up to 2 x 8 x 0.266 = 4.26 GB/s

## Slide 61: 2. Evolution of Intel’s high performance multicore MP server platforms (21)
Obviously, in SMP configurations with higher core count and memory speeds, a single FSB
may severely limit memory bandwidth and thus performance.
This FSB caused bandwidth bottleneck may resolved by using more than one FSB, as indicated
in the subsequent Figures.
Resolving the FSB bottleneck in SMP configurations -1

## Slide 62
Xeon MP1
SC
Xeon MP1
SC
FSB (400 MT/s)
Xeon MP1
SC
Xeon MP1
SC
Preceding ICH
Preceding NBs
E.g. HI 1.5
HI 1.5 266 MB/s
E.g. DDR-200/266
E.g. DDR-200/266
90 nm Pentium 4 Prescott MP aimed
Truland MP server platform (for up to 2 C)
(2006)
Previous Pentium 4 MP aimed
MP server platform (for single core processors)
(2004 and before)
85001/8501
ICH5
XMB
XMB
DDR-266/333
DDR2-400
XMB
XMB
HI 1.5
DDR-266/333
DDR2-400
Resolving the FSB bottleneck by using dual FSBs in dual core MP server platforms
2. Evolution of Intel’s high performance multicore MP server platforms (22)
FSB
(800 MT/s)
Xeon 7000
(Paxville MP) 2x1C
Xeon 7100
(Tulsa) 2C
Xeon MP
(Potomac) 1C
/
/
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
IMI
IMI

## Slide 63
85001/8501
ICH5
XMB
XMB
DDR-266/333
DDR2-400
FSB
(800 MT/s)
XMB
XMB
HI 1.5
DDR-266/333
DDR2-400
Xeon 7000
(Paxville MP) 2x1C
Xeon 7100
(Tulsa) 2C
Xeon MP
(Potomac) 1C
/
/
1 The E8500 MCH supports an FSB of 667 MT/s and consequently only the SC Xeon MP (Potomac)
90 nm Pentium 4 Prescott MP aimed
Truland MP server platform (for up to 2 C)
(2006)
Core 2 aimed
Caneland MP server platform (for up to 6 C)
(2007)
ESI: Enterprise System Interface
4 PCIe lanes, 0.25 GB/s per lane (like the DMI interface,
providing 1 GB/s transfer rate in each direction)
HI 1.5 (Hub Interface 1.5)
8 bit wide, 66 MHz clock, QDR,
266 MB/s peak transfer rate
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
7300
631xESB/ 632xESB
up to
8 DIMMs
ESI
FBDIMM
DDR2-533/667
2. Evolution of Intel’s high performance multicore MP server platforms (23)
Resolving the FSB bottleneck by using quad FSBs in up to 6 core MP server platforms
Core2 (2C/4C)
Penryn (6C)
Core2 (2C/4C)
Penryn (6C)
Core2 (2C/4C)
Penryn (6C)
Core2 (2C/4C)
Penryn (6C)
FSB
(1066 MT/s)
Xeon 7200
(Tigerton DC) 1x2C
Xeon 7300
(Tigerton QC) 2x2C
Xeon 7400
(Dunnington 6C)
/
/
IMI
IMI

## Slide 64
Platform | Platform topology | Date of intro. | Processor | Techno- logy | Core count (up to) | No./kind of the links to mem. buffers | No. of mem. channels/ mem. buffer | No. /speed of mem. channels (up to)
Truland MP | SMP w/dual FSBs | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 90 nm | 1C | 4 serial IMI channels from MCH to XMBs | 2 memory channels/ XMB | 2x DDR2-800/ socket
 |  | 11/2005 | Xeon 7000 (Paxville MP) | 90 nm | 2x1C |  |  | 
 |  | 8/2006 | Xeon 7100 (Tulsa) | 65 nm | 2C |  |  | 
Caneland | SMP w/Quad FSBs | 9/2007 | Xeon 7200 Tigerton DC (Core 2) | 65 nm | 2C | 4 serial FB-DIMM channels from MCH to AMBs | 1 memory channel/ AMB | 1x DDR2-667/ socket
 |  | 9/2007 | Xeon 7300 Tigerton QC (Core 2) | 65 nm | 2x2C |  |  | 
 |  | 9/2008 | Xeon 7400 (Dunnington) (Penryn) | 45 nm | 6C |  |  | 
Boxboro-EX | NUMA fully connect. by QPI buses | 3/2010 | Nehalem-EX (Xeon 7500/ (Beckton) | 45 nm | 8C | 4 serial SMI channels per proc. to 4 SMBs | 2 memory channels/ SMB | 8x DDR3-1067/ socket
 |  | 4/2011 | Westmere-EX (E7-4800) | 32 nm | 10C |  |  | 
Brickland | NUMA fully connect. by QPI buses | 2/2014 | Ivy Bridge-EX (E7-4800 v2) | 22 nm | 15C | 4 parallel SMI2 channels per proc. to 4 SMBs | 2 memory channels/ SMB | 8x DDR3-1600 (IWB) / DDR4-1866 (HSW)/ socket
 |  | 5/2015 | Haswell-EX (E7-4800 v3) | 22 nm | 18C |  |  | 
 |  | Q2/2016 | Broadwell-EX | 14 nm | 24C |  |  | 
Purley | NUMA fully connect. by UPI buses | 2017 | Skylake-EX | 14 nm | 28C | 6 channels per proc. | n.a. | DDR4-2666 mem. speed
Evolution of Intel’s high performance MP platforms – Memory architecture
2. Evolution of Intel’s high performance multicore MP server platforms (24)

## Slide 65
Xeon MP1
SC
Xeon MP1
SC
FSB
Xeon MP1
SC
Xeon MP1
SC
Preceding ICH
Preceding NBs
E.g. HI 1.5
HI 1.5 266 MB/s
E.g. DDR-200/266
E.g. DDR-200/266
85001/8501
ICH5
XMB
XMB
DDR-266/333
DDR2-400
FSB
XMB
XMB
HI 1.5
DDR-266/333
DDR2-400
Xeon 7000
(Paxville MP) 2x1C
Xeon 7100
(Tulsa) 2C
Xeon MP
(Potomac) 1C
/
/
90 nm Pentium 4 Prescott MP aimed
Truland MP server platform (for up to 2 C)
(2006)
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
Previous Pentium 4 MP aimed
MP server platform (for single core processors)
(2004 and before)
Evolution of single core MP server platforms to dual core MP server platform
2. Evolution of Intel’s high performance multicore MP server platforms (25)
IMI
IMI
IMI (Independent Memory Interface): Low line count (70 signal lines) serial interface vs. DDR2 with 240 pins.
XMB: eXternal Memory Bridge

## Slide 66
Core2 (2C/4C)
Penryn (6C)
Core2 (2C/4C)
Penryn (6C)
Core2 (2C/4C)
Penryn (6C)
Core2 (2C/4C)
Penryn (6C)
7300
631xESB/ 632xESB
up to
8 DIMMs
85001/8501
ICH5
XMB
XMB
DDR-266/333
DDR2-400
FSB
XMB
XMB
ESI
FSB
HI 1.5
DDR-266/333
DDR2-400
4 x FB-DIMM
DDR2-533/667
Xeon 7000
(Paxville MP) 2x1C
Xeon 7100
(Tulsa) 2C
Xeon MP
(Potomac) 1C
/
/
1 The E8500 MCH supports an FSB of 667 MT/s and consequently only the SC Xeon MP (Potomac)
Xeon 7200
(Tigerton DC) 1x2C
Xeon 7300
(Tigerton QC) 2x2C
Xeon 7400
(Dunnington 6C)
/
/
90 nm Pentium 4 Prescott MP aimed
Truland MP server platform (for up to 2 C)
(2006)
Core 2 aimed
Caneland MP server platform (for up to 6 C)
(2007)
ESI: Enterprise System Interface
4 PCIe lanes, 0.25 GB/s per lane (like the DMI interface,
providing 1 GB/s transfer rate in each direction)
HI 1.5 (Hub Interface 1.5)
8 bit wide, 66 MHz clock, QDR,
266 MB/s peak transfer rate
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
Evolution of dual core MP server platform to up to 6 core MP platform
2. Evolution of Intel’s high performance multicore MP server platforms (26)

## Slide 67: 2. Evolution of Intel’s high performance multicore MP server platforms (27)
A brief introduction to FB-DIMM memories
FB-DIMM memories were standardized and introduced in the 2006/2007 timeframe .
They supported DDR2 memories up to DDR2-667.
FB-DIMMs connect the MC and the DIMMs via low line count serial buses whereby the
memory buffers providing serial/parallel conversion to the DIMMs are placed onto the
DIMMs, as shown in the next Figure.

## Slide 68: 2. Evolution of Intel’s high performance multicore MP server platforms (28)
Figure: FB-DIMM memory architecture [102]
Layout of an FB-DIMM based memory subsystem -1 [102]

## Slide 69: 2. Evolution of Intel’s high performance multicore MP server platforms (29)
Comparing the number of sctive signal lines in RDIMM and FB-DIMM channels [129]

## Slide 70: 2. Evolution of Intel’s high performance multicore MP server platforms (30)
The standardized FB-DIMM technology supports a cascaded connection of up to 8 FB-DIMMs
to a memory controller by a packet based, bidirectional, point-to-point link.
The link make use of differential signaling and includes 14 read/10 write lanes, as indicated
in the next Figure.
Layout of an FB-DIMM based memory subsystem -2 [102]

## Slide 71: 2. Evolution of Intel’s high performance multicore MP server platforms (31)
Figure: FB-DIMM memory architecture [102]
Layout of an FB-DIMM based memory subsystem -3 [102]

## Slide 72: 2. Evolution of Intel’s high performance multicore MP server platforms (32)
The 14 inbound lanes carry data from the memory to the memory controller whereas the
10 outbound lanes transfer commands and data from the memory controller to the memory.
The transfer rate is 6 times the transfer rate of the memory, i.e. 6x667=4 MT/s over the
differential lines.
Data and commands, transferred in 12 cycles, from one frame, that is an inbound frame includes
12x14=168 bit whereas an outbound frame has 12x10=120 bits.
For more information we refer to the literature, e.g. [103].
Layout of an FB-DIMM based memory subsystem -4 [103]

## Slide 73: 2. Evolution of Intel’s high performance multicore MP server platforms (33)
Reasoning for using FB-DIMM memory in the Caneland platform
As FB-DIMMs need only about 1/3 of the active lines compared to standard DDR2 DIMMs,
significantly more memory channels (e.g. 6 channels) may be connected to the MCH than
in case of high pin count DDR2 DIMMs.
Furthermore, due to the cascaded interconnection of the FB-DIMMs (with repeater
functionality), up to 8 DIMMs may be interconnected to a single DIMM channel instead of
two or three as typical for standard DDR2 memory channels.
This results in considerably more memory bandwidth and memory size by reduced mainboard
complexity.
Based on these benefits Intel decided to use FB-DIMM-667 memory in their server platforms,
first in their DP platforms already in 2006 followed by the Caneland MP platform in 2007,
as discussed before.

## Slide 74
Nehalem-EX 8C
Westmere-EX 10C
7500 IOH
QPI
QPI
QPI
QPI
QPI
QPI
QPI
QPI
SMB
SMB
Nehalem-EX: up to DDR3-1067
Westmere-EX: up to DDR3-1333
SMB
SMB
SMB
SMB
SMB
SMB
ICH10
ESI
SMI: Scalable Memory Interface
(Serial link between the
processor and the SMB)
(Differential signaling, ~25 lanes)
SMB: Scalable Memory Buffer
(Conversion between the serial SMI and the parallel DDR3 DIMM interfaces)
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI
channels
2x4 SMI
channels
Main enhancements of the Nehalem-EX/Westmere-EX aimed up to 10 core Boxboro-EX
4S server platform (assuming 1 IOH)
ME
ME: Management Engine
Xeon 7500
(Nehalem-EX)
(Becton) 8C
Xeon E7-4800
(Westmere-EX) 10C
Nehalem-EX 8C
Westmere-EX 10C
Nehalem-EX 8C
Westmere-EX 10C
Nehalem-EX 8C
Westmere-EX 10C
/
Nehalem-EX aimed Boxboro-EX MP server platform (for up to 10 C)
(2010/2011)
2 DIMMs/memory channel
4 x QPI up to 6.4 GT/s
36
PCIe
2.0
2. Evolution of Intel’s high performance multicore MP server platforms (34)

## Slide 75: 2. Evolution of Intel’s high performance multicore MP server platforms (35)
Returning to the stand alone memory buffer implementation in the Boxboro-EX
MP platform from using FB-DIMMs -1
FB-DIMM memories were introduced in the 2006/2007 timeframe and supported DDR2
memories up to DDR2-667.
Due to inherent drawbacks of FB-DIMM memories, such as higher dissipation caused by the
DA/AD conversions, longer access time due to the cascaded nature of accessing the DIMMs
and higher price, FB-DIMMs reached only a small market share.
This was the reason why memory vendors were reluctant to develop DDR3-based FB-DIMM
memory modules and why Intel was forced to move back to custom DDR3 DIMMs in their
Boxboro-EX platform.

## Slide 76: 2. Evolution of Intel’s high performance multicore MP server platforms (36)
Implementing memory extension buffers MBs)
Implementing stand alone MBs
mounted on the mainboard or
on a riser card
Implementing MBs
immediately on the DIMM
(called FB-DIMMs)
Truland MP platform
(2005/2006)
Caneland platform
(2007/2008)
Boxboro-EX platform
(2010/2011)
Brickland platform
(2014/2015)
Figure: Intel’s implementation of memory extension buffers
Returning to the stand alone memory buffer implementation in the Boxboro-EX
MP platform from using FB-DIMMs -2

## Slide 77: 2. Evolution of Intel’s high performance multicore MP server platforms (37)
C602J PCH
(Patsburg J)
QPI
1.1
QPI
1.1
QPI 1.1
QPI 1.1
QPI 1.1
QPI 1.1
DMI2
4xPCIe2
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI2
channels
2x4 SMI2
channels
Main enhancement of the up to 15 core Ivy Bridge-EX aimed Brickland 4S server platform
ME
ME: Management Engine
Xeon E7-4800 v2
(Ivy Bridge-EX)
(Ivytown) 15C
Ivy Bridge-EX 15C
Ivy Bridge-EX 15C
Ivy Bridge-EX 15C
3 x QPI up to 8.0 GT/s
SMI2: Scalable Memory Interface 2
(Parallel 64 bit VMSE data link between
the processor and the SMB)
SMB: Scalable Memory Buffer
(C102/C104: Jordan Creek)
(Performs conversion between the
parallel SMI2 and the parallel
DDR3-DIMM interfaces)
C102: 2 DIMMs/channel
C104: 3 DIMMs/channel
Ivy Bridge-EX 15C
PCIe 3.0
32
PCIe 3.0
32
PCIe 3.0
32
PCIe 3.0
32
Up to DDR3-1600 in lockstep mode and
up to DDR3-1333 in independent channel mode

## Slide 78: 2. Evolution of Intel’s high performance multicore MP server platforms (38)
ME: Management Engine
3x QPI 1.1: Up to 9.6 GT/s
QPI
1.1
QPI
1.1
QPI 1.1
QPI 1.1
QPI 1.1
QPI 1.1
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI2
channels
2x4 SMI2
channels
Xeon E7-4800 v3
(Haswell-EX) 18C
Haswell-EX 18C
Haswell--EX 18C
Haswell-EX 18C
Haswell-EX 18C
SMI2: Scalable Memory Interface 2
(Parallel 64-bit VMSE data link between
the processor and the SMB)
(~110 bidirectional VMSE data lines)
SMB: Scalable Memory Buffer
(C112/C114: Jordan Creek 2)
(Performs conversion between the
parallel SMI2 and the parallel
DDR3/DDR4 DIMM interfaces)
C112: 2 DIMMs/channel
C114: 3 DIMMs/channel
Up to DDR3-1600
in both indep. channel and lockstep modes and
up to DDR4-1866 in lockstep mode
PCIe 3.0
32
PCIe 3.0
32
C602J PCH
(Patsburg J)
DMI2
4xPCIe2
ME
PCIe 3.0
32
PCIe 3.0
32
Main enhancements of the up to 18 core Haswell-EX aimed Brickland 4S server platform

## Slide 79: 2. Evolution of Intel’s high performance multicore MP server platforms (39)
Microarchitecture of the18 core Haswell-EX processor [111]

## Slide 80: 2. Evolution of Intel’s high performance multicore MP server platforms (40)
Microarchitecture of the ARMv8-based dual socket Cavium ThunderX processor [128]

## Slide 81: 2. Evolution of Intel’s high performance multicore MP server platforms (41)
b) Redesigned SMI 2 interface between the processor and the memory buffers
resulting in reduced dissipation
The SMI link of the Boxboro-EX platform was a serial, packet based, differential link
including about 70 signal lines.
By contrast, as far as the data transfer is concerned, with the SMI2 link Intel changed to
64-bit parallel, bidirectional communication using single-ended voltage reference signals,
called VMSE (Voltage Mode Single Ended) signaling.
SMI 2 requires altogether about 110 signal lines, that is about 50 % more lines than SMI.
The reason for changing from serial transfer to parallel transfer in case of the data lines is
presumably the fact, that in this case AD/DA converting of data becomes superfluous and
this results in reduced dissipation.

## Slide 82
Platform | Platform topology | Date of intro. | Processor | Techno- logy | Core count (up to) | L2 cache | L3 cache
Truland MP | SMP w/dual FSBs | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 90 nm | 1C | 1 MB | 8 MB
 |  | 11/2005 | Xeon 7000 (Paxville MP) | 90 nm | 2x1C | 2 MB L2/C | --
 |  | 8/2006 | Xeon 7100 (Tulsa) | 65 nm | 2C | 1 MB L2/C | 16 MB
Caneland | SMP w/Quad FSBs | 9/2007 | Xeon 7200 Tigerton DC (Core 2) | 65 nm | 2C | 4 MB/C | --
 |  | 9/2007 | Xeon 7300 Tigerton QC (Core 2) | 65 nm | 2x2C | 4 MB/C | ---
 |  | 9/2008 | Xeon 7400 (Dunnington) (Penryn) | 45 nm | 6C | 3 MB/C | 16 MB
Boxboro-EX | NUMA fully connect. by QPI buses | 3/2010 | Nehalem-EX (Xeon 7500/ (Beckton) | 45 nm | 8C | ¼ MB/C | 24 MB
 |  | 4/2011 | Westmere-EX (E7-4800) | 32 nm | 10C | ¼ MB/C | 30 MB
Brickland | NUMA fully connect. by QPI buses | 2/2014 | Ivy Bridge-EX (E7-4800 v2) | 22 nm | 15C | ¼ MB/C | 37.5 MB
 |  | 5/2015 | Haswell-EX (E7-4800 v3) | 22 nm | 18C | ¼ MB/C | 35 MB
 |  | Q2/2016 | Broadwell-EX | 14 nm | 24C | ¼ MB/C | 60 MB
Purley | NUMA fully connect. by UPI buses | 2017 | Skylake-EX | 14 nm | 28C | n.a. | n.a.
Intel’s high performance MP platforms – Cache architectures
2. Evolution of Intel’s high performance multicore MP server platforms (42)

## Slide 83
Platform | Platform topology | Date of intro. | Processor | Techno- logy | Core count (up to) | FSB/QPI | IF to chipset | PCIe
Truland MP | SMP w/dual FSBs | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 90 nm | 1C | 2xFSB 667 MT/s | HI1.5 (266 MB/s bidirectional) | 28 x PCIe lanes on the MCH
 |  | 11/2005 | Xeon 7000 (Paxville MP) | 90 nm | 2x1C | 2xFSB 800 MT/s |  | 
 |  | 8/2006 | Xeon 7100 (Tulsa) | 65 nm | 2C |  |  | 
Caneland | SMP w/Quad FSBs | 9/2007 | Xeon 7200 Tigerton DC (Core 2) | 65 nm | 2C | 4xFSB 1066 MT/s | ESI x4 (4x PCIe lanes) (1GB/s per direction) | 28 x PCIe lanes on the MCH
 |  | 9/2007 | Xeon 7300 Tigerton QC (Core 2) | 65 nm | 2x2C |  |  | 
 |  | 9/2008 | Xeon 7400 (Dunnington) (Penryn) | 45 nm | 6C |  |  | 
Boxboro-EX | NUMA fully connect. by QPI buses | 3/2010 | Nehalem-EX (Xeon 7500/ (Beckton) | 45 nm | 8C | 4xQPI 6.4 GT/s (3 for NUMA) | QPI (6.4 GB/s) | 36 x PCIe 2.0 lanes on the IOH
 |  | 4/2011 | Westmere-EX (E7-4800) | 32 nm | 10C |  |  | 
Brickland | NUMA fully connect. by QPI buses | 2/2014 | Ivy Bridge-EX (E7-4800 v2) | 22 nm | 15C | 3xQPI 1.1 8 GT/s | DMI2 x4 (4xPCIe 2.0) (2 GB/s per direction) | 32 x PCIe 3.0 lanes on the proc.
 |  | 5/2015 | Haswell-EX (E7-4800 v3) | 22 nm | 18C | 3xQPI 1.1 9.6 GT/s |  | 
 |  | Q2/2016 | Broadwell-EX | 14 nm | 24C | 3xQPI 1.1 |  | 
Purley | NUMA fully connect. by UPI buses | 2017 | Skylake-EX | 14 nm | 28C | 3xUPI 10.4 GT/s | DMI3 x4 (4xPCIe 3.0) (~ 4GB/s/dir. | 48 x PCIe lanes on the proc.
Intel’s high performance MP platforms – Connectivity
2. Evolution of Intel’s high performance multicore MP server platforms (43)

## Slide 84
3. Example 1: The Brickland platform
3.1 Overview of the Brickland platform
3.3 The Ivy Bridge-EX (E7-4800 v2) 4S processor line
3.4 The Haswell-EX (E7-4800 v3) 4S processor line
3.5 The Broadwell-EX (E7-4800 v4) 4S processor line
3.2 Key innovations of the Brickland platform vs.
the previous Boxboro-EX platform
Notes: 84

## Slide 85
3.1 Overview of the Brickland platform
Notes: 85

## Slide 86: 3.1 Overview of the Brickland platform (1)
3.1 Overview of the Brickland platform
Positioning the Brickland platform [112]

## Slide 87: 3.1 Overview of the Brickland platform (2)
Xeon E7-4800 v2
Xeon
E7-4800 v3
5/2015
3/2012
C602J
(Ivy Bridge-EX)
(Ivytown) 15C
(Haswell-EX) 14C
Brickland
2/2014
(Patsburg J)
Attached via x4 DMI2
22 nm/4310 mtrs/541 mm2
¼ MB L2/C
37.5 MB L3
3 QPI 1.1 links 8 GT/s
4 SMI2 links to 4 SMBs
2 mem. channels/SMB
up to 3 DIMMs/mem. channel
up to DDR3-1600 MT/s
6 TB (96x64 GB)
32 PCIe 3.0
LGA 2011-1
22 nm/5560 mtrs/661 mm2
¼ MB L2/C
35 MB L3
3 QPI 1.1 links 9.6 GT/s
4 SMI2 links to 4 SMBs
2 mem. channels/SMB
up to 3 DIMMs/mem. channel
up to DDR4-1866 MT/s
6 TB (96x64 GB)
32 PCIe 3.0
LGA 2011-1
Ivy Bridge-EX-based
22 nm
2/2014
Haswell-EX based
22 nm
MP platforms
MP cores
PCH
Ivy Bridge-EX based
Haswell-EX based
The Brickland platform

## Slide 88: 3.1 Overview of the Brickland platform (3)
C602J PCH
(Patsburg J)
QPI
1.1
QPI
1.1
QPI 1.1
QPI 1.1
QPI 1.1
QPI 1.1
DMI2
4xPCIe2
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI2
channels
2x4 SMI2
channels
ME
Xeon E7-4800 v2
(Ivy Bridge-EX)
(Ivytown) 15C
Ivy Bridge-EX
Haswell-EX
Ivy Bridge-EX
Haswell-EX
Ivy Bridge-EX Haswe-EX
Ivy Bridge-EX
Haswell_EX
PCIe 3.0
32
PCIe 3.0
32
PCIe 3.0
32
PCIe 3.0
32
Xeon E7-4800 v3
(Haswell-EX)
14C
/
Basic system architecture of the Brickland 4S server platform (2014/2015)
(assuming 2x3 DIMMs/SMB)
SMB: Scalable Memory Buffer
(Performs conversion between the
parallel SMI2 and the parallel
DIMM interfaces)
SMI2: Scalable Memory Interface 2
(Parallel 64 bit VMSE data link between
the processor and the SMB)

## Slide 89: 3.1 Overview of the Brickland platform (4)
Feature | Ivy Bridge-EX based (E7-4800 v2) | Haswell-EX based (E7-4800 v3)
Cores | Up to 15 | Up to 14
LLC3 size | Up to 15x2.5 MB | Up to 14x2.5 MB
QPI | 3xQPI 1.1 Up to 8.0 GT/s in both dir. (16 GB/s per dir.) | 3xQPI 1.1 Up to 9.6 GT/s in both dir. (19.2 GB/s per dir.)
SMB | C102/C104 (Jordan Creek) C102: 2 DIMMs/SMB C103: 3 DIMMs/SMB | C112/C114 (Jordan Creek 2) C102: 2 DIMMs/SMB C103: 3 DIMMs/SMB
VMSE speed | Up to 2667 MT/s | Up to 3200 MT/s
DDR4 speed | n.a. | Perf. mode: up to 1600 MT/s Lockstep mode: up to 1866 MT/s
DDR3 speed | Perf. mode: up to 1333 MT/s Lockstep mode: up to 1600 MT/s | Perf. mode: up to 1600 MT/s Lockstep mode: up to 1600 MT/s
Contrasting differences in key features of the Ivy Bridge-EX and Haswell-EX based
Brickland platforms [114]

## Slide 90
3.2 Key innovations of the Brickland platform vs.
the previous Boxboro-EX platform
Notes: 90

## Slide 91: 3.2 Key innovations of the Brickland platform (1)
3.2 Key innovations of the Brickland platform vs. the previous Boxboro-EX platform
3.2.1 Connecting PCIe links direct to the processors rather than to the MCH
3.2.2 New memory buffer design

## Slide 92: 3.2 Key innovations of the Brickland platform (2)
3.2.1 Connecting PCIe links direct to the processors rather than to the MCH -1
3.2.1.1 Overview
36 lanes of PCIe 2.0
2 x QPI
Boxboro platform [106]
Brickland platform [114]

## Slide 93: 3.2 Key innovations of the Brickland platform (3)
Connecting PCIe links direct to the processors rather than to the MCH -2
It has two major implications, including
Raising the PCIe lane count provided by the Brickland platform (see Section 3.2.1.2)
Reducing the bandwidth needed between the processors and the chipset (see Section 3.2.1.3)

## Slide 94: 3.2 Key innovations of the Brickland platform (4)
As long as the Boxboro-EX platform provides 36 PCIe lanes, the Brickland platform affords
32 PCIe lanes per processor, i.e. 4 x 32 = 132 lanes in total for a 4S platform, as shown below.
3.2.1.2 Raising the PCIe lane count provided by the Brickland platform -1
36 lanes of PCIe 2.0
2 x QPI
Boxboro platform
Brickland platform
Figure: Connecting PCIe links direct to the processors rather than to the MCH

## Slide 95: 3.2 Key innovations of the Brickland platform (5)
3.2.1.2 Raising the PCIe lane count provided by the Brickland platform -2
If the PCI lanes are connected directly to the processors rather than to the MCH, the number of PCIe lanes supported by the platform will scale linearly with the number of processors.
In addition, the Brickland platform provides faster PCIe 3.0 lanes instead of PCI 2.0 lanes
of the previous Boxboro platform.

## Slide 96: 3.2 Key innovations of the Brickland platform (6)
3.2.1.3 Reducing the bandwidth demand between the processors and the chipset
By relocating the PCIe links from the MCH to the processors, the bandwidth needed
between the chipset and the processors becomes significantly reduced, as follows;
In the preceding Boxboro platform the MCH provides 36 PCIe 2.0 lanes with a total
bandwidth of 36x0.5 GB/s = 18 GB/s per direction.
This gives rise for using a QPI 1.1 bus width the bandwidth of 16.0 GB/s per direction
between the MCH and the processors.
By contrast, in the Brickland platform the PCIe lanes are connected immediately to the
processors and there is no need for providing the associated bandwidth.
This has three consequences;
Interconnecting the processors and the PCH by a DMI2 (4x PCIe 2.0) link
Providing only three QPI links per processor
Implementing a single chip “chipset”,
as discussed next.

## Slide 97: 3.2 Key innovations of the Brickland platform (7)
Due to the reduced bandwidth demand of the chipset-processor interface, it suffices now
to interconnect the PCH with a single processor via a DMI2 interface consisting of 4 PCIe 2.0
lanes that provide a bandwidth of up to 4x0.5=2 GB/s, rather than using a QPI bus with
a bandwidth of 16.0 GB/s.
a) Interconnecting the processors and the PCH by a DMI2 (4x PCIe 2.0) interface
Figure: The Haswell-EX implementation of the Brickland platform [114]

## Slide 98: 3.2 Key innovations of the Brickland platform (8)
b) Providing only three QPI links per processor -1
As the Brickland platform does not need an extra QPI bus to interconnect the processor with
the PCH, it has only 3 QPI buses per processor rather than four compared to the previous
(Boxboro-EX) platform, as shown in the next Figure.
Figure: The Haswell-EX implementation of the Brickland platform [114]

## Slide 99: 3.2 Key innovations of the Brickland platform (9)
Providing only three QPI links per processor -2
In addition, the Brickland platform supports already QPI 1.1 buses with the following speeds:
Ivy Bridge-EX based Brickland platforms: up to 8.0 Gbps
Nehalem-EX based Brickland platforms: up to 9.6 Gbps

## Slide 100: 3.2 Key innovations of the Brickland platform (10)
c) Implementing a single chip “chipset”
Inspired by the reduced functionality, the chipset is now implemented as a single chip solution
instead of using two chips, as in the previous Boxboro platform.
The single chip “chipset” is now designated as the PCH (Platform Controller Hub).
It is in particular the C602 J or Patsburg-J PCH, as shown below.
Figure: The Haswell-EX implementation of the Brickland platform [114]

## Slide 101: 3.2 Key innovations of the Brickland platform (11)
3.2.2 New memory buffer design
a) Redesigned, basically parallel MC-SMB interface, called SMI2 interface
b) Enhanced DRAM interface
It has two main components, as follows:

## Slide 102: 3.2 Key innovations of the Brickland platform (12)
a) Redesigned, basically parallel MC-SMB interface, called SMI2 interface -1
Scalable Memory Buffer
(SMB)
SMI2 data
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
SMI CMD
DDR3/4
interface
Scalable Memory Buffer
(SMB)
SMI In
DIMM
DIMM
DIMM
DIMM
SMI Out
DDR3
interface
Boxboro-EX platform
Brickland platform
SMI: Serial, packet based, unidirectional links
with differential signaling
Up to 6.4 Gbps
SMI 2: 64-bit parallel, bidirectional data link
with single-ended voltage referenced signaling,
(VMSE (Voltage Mode single Ended) signaling)
Up to 3200 MT/s
(14 lanes)
(11 lanes)

## Slide 103: 3.2 Key innovations of the Brickland platform (13)
The SMI link of the Boxboro-EX platform was a serial, packet based,unidirectional link
with differential signaling, including about 70 signal lines.
By contrast, as far as the data transfer is concerned, with the SMI2 link Intel changed to
64-bit parallel, bidirectional communication using single-ended voltage reference signals,
called VMSE (Voltage Mode Single Ended) signaling.
SMI 2 requires altogether about 110 signal lines, that is about 50 % more lines than SMI.
The reason for changing from serial transfer to parallel transfer in case of the data lines is
presumably the fact, that in this case AD/DA converting of data becomes superfluous and
this results in reduced dissipation.
The SMI 2 operates
in the Ivy Town-EX based Brickland platform at a speed of up to 2667 MT/s and
in the Haswell-EX based Brickland platform at a speed of up to 3200 MT/s.
a) Redesigned, basically parallel MC-SMB interface, called SMI2 interface -2

## Slide 104: 3.2 Key innovations of the Brickland platform (14)
b) Enhanced DRAM interface
Scalable Memory Buffer
(SMB)
SMI2 data
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
SMI CMD
DDR3/4
interface
Scalable Memory Buffer
(SMB)
SMI In
DIMM
DIMM
DIMM
DIMM
SMI Out
DDR3
interface
Boxboro-EX platform
Brickland platform
Up to DDR3-1333
Up to 2 DIMMs per memory channel
Up to DDR4-1866
Up to 3 DIMMs per memory channel
(11 lanes)
(14 lanes)

## Slide 105: 3.2 Key innovations of the Brickland platform (15)
Operation modes of the SMBs in the Brickland platform [113]
Operation modes of the SMBs
Lockstep mode
Independent channel mode
(aka Performance mode)
In lockstep mode the same command is sent
on both DRAM buses.
The read or write commands are issued
simultaneously to the referenced DIMMs,
and the SMB interleaves the data on the
In the independent channel mode commands
sent to both DRAM channels are independent
from each other.

## Slide 106: 3.2 Key innovations of the Brickland platform (16)
DRAM speeds of the Brickland platform
Feature | Ivy Bridge-EX based (E7-4800 v2) | Haswell-EX based (E7-4800 v3)
SMB | C102C104 | C112/C114
DDR4 speed | n.a. | Independent mode: up to 1600 MT/s Lockstep mode: up to 1866 MT/s
DDR3 speed | Independent mode: up to 1333 MT/s Lockstep mode: up to 1600 MT/s | Independent mode: up to 1600 MT/s Lockstep mode: up to 1600 MT/s

## Slide 107: 3.2 Key innovations of the Brickland platform (17)
E7-8800 v3 /E7-4800 v3 family
(18-Core), w/ QPI up to 9.6 GT/s
Haswell-EX
Example for a Haswell-EX based Brickland platform [115]

## Slide 108
3.3 The Ivy Bridge-EX (E7-4800 v2) 4S processor line
Notes: 108

## Slide 109: 3.3 The Ivy Bridge-EX (E7-4800 v2) 4S processor line (1)
Intel developed a single processor to cover all server market segments from 1S to 8S, called
the Ivytown processor.
3.3 The Ivy Bridge-EX (4800 v2) 4S processor line [116]
It is manufactured on the 22 nm technology, includes up to 15 cores built up on 4.31 billion
transistors on a die of 541 mm2.
Ivytown processor versions have a TDP of 40 to 150 W and operate at frequencies ranging
from 1.4 to 3.8 GHz.
The Ivytown processor was launched along with the Romley 2S server platform in 9/2013
followed by the Brickland 4S platform in 2/2014.

## Slide 110: 3.3 The Ivy Bridge-EX (E7-4800 v2) 4S processor line (2)
Ivytown processor alternatives for different server platforms 117]
Entry level
E5 v2 2400 1, 2 sockets
Performance level
E5 v2 2600 1, 2. 4 sockets
High-performance level
E7 v2 4800/8800
2, 4, 8 sockets
E5 platform: Romley
E7 platform: Brickland

## Slide 111: 3.3 The Ivy Bridge-EX (E7-4800 v2) 4S processor line (3)
E5, E7 platform alternatives built up of Ivytown processors [117]
Romley Entry and Performance level platform alternatives
Brickland High performance platform alternatives

## Slide 112: 3.3 The Ivy Bridge-EX (E7-4800 v2) 4S processor line (4)
Block diagram of the Ivy Town processor
PCU: Power Control Unit
TAP: Test Access Port
FUSE: Fuse block, to configure the die
i.e. to have various core and
cache sizes as well as
different frequency and TDP
levels
DRNG: Digital Random Number
Generator
IIO: Integrated I/O block
HA: Home Agent providing
memory coherency
MC: Memory Controller
VMSE: Voltage-Mode Single-Ended
Interface (actually the
SMB)
The processor consists of 3 slices, each with 5 cores and associated LLC segments, as seen below.
Figure: Block diagram of the Ivy Town processor [116]

## Slide 113: 3.3 The Ivy Bridge-EX (E7-4800 v2) 4S processor line (5)
Layout of the ring interconnect bus used for dual slices (10 cores) [125]

## Slide 114: 3.3 The Ivy Bridge-EX (E7-4800 v2) 4S processor line (6)
Layout of the ring interconnect bus used for three slices (15 cores) [125]
There are 3 virtual rings.
Multiplexers (MUXs) dynamically interconnect the rings, as shown below.
Clockwise outer ring
Counter-clockwise outer ring
Figure: Three-slice ring interconnect with three virtual rings interconnected by multiplexers [125]

## Slide 115: 3.3 The Ivy Bridge-EX (E7-4800 v2) 4S processor line (7)
Implementing lower core variants through chopping [116]

## Slide 116: 3.3 The Ivy Bridge-EX (E7-4800 v2) 4S processor line (8)
Lower core alternatives of the Ivytown processor achieved by chopping [116]
15 cores
10 cores
6 cores

## Slide 117: 3.3 The Ivy Bridge-EX (E7-4800 v2) 4S processor line (9)
TDP vs. core frequency in different Ivytown processor alternatives [116]

## Slide 118
3.4 The Haswell-EX (E7-4800 v3) 4S processor line
Notes: 118

## Slide 119: 3.4 The Haswell-EX (E7-4800 v3) 4S processor line (1)
3.4 The Haswell-EX (E7-4800 v3) 4S processor line
Launched in 5/2015
22 nm, 5.7 billion transistors, 662 mm, up to 18 cores
Number of cores
Up to 18 cores for 8S processors
Up to 14 cores for 4S ones (in 08/2015) instead 18 cores

## Slide 120: 3.4 The Haswell-EX (E7-4800 v3) 4S processor line (2)
Basic layout of an 18 core 8S Haswell-EX v3 (E7-8800) processor [118]

## Slide 121: 3.4 The Haswell-EX (E7-4800 v3) 4S processor line (3)
Feature | Ivy Bridge-EX (E7-4800 v2) | Haswell-EX (E7-4800 v3)
Cores | Up to 15 | Up to 14
LLC size (L3) | Up to 15x2.5 MB | Up to 14x2.5 MB
QPI | 3xQPI 1.1 Up to 8.0 GT/s in both dir. (16 GB/s per dir.) | 3xQPI 1.1 Up to 9.6 GT/s in both dir. (19.2 GB/s per dir.)
SMB | C102/C104 (Jordan Creek) C102: 2 DIMMs/SMB C103: 3 DIMMs/SMB | C112/C114 (Jordan Creek 2) C102: 2 DIMMs/SMB C103: 3 DIMMs/SMB
VMSE speed | Up to 2667 MT/s | Up to 3200 MT/s
DDR4 speed | n.a. | Perf. mode: up to 1600 MT/s Lockstep mode: up to 1866 MT/s
DDR3 speed | Perf. mode: up to 1333 MT/s Lockstep mode: up to 1600 MT/s | Perf. mode: up to 1600 MT/s Lockstep mode: up to 1600 MT/s
TSX | n.a. | Supported
Contrasting key features of the Ivy Bridge-EX and Haswell-EX processors -1 [114]

## Slide 122: 3.4 The Haswell-EX (E7-4800 v3) 4S processor line (4)
We note that the Haswell-EX processors support Intel’s Transactional Synchronization Extension
(TSX) that has been introduced with the Haswell core, but became disabled in the Haswell-EP
processors due to a bug.
Contrasting key features of the Ivy Bridge-EX and Haswell-EX processors -1 [114]

## Slide 123: 3.4 The Haswell-EX (E7-4800 v3) 4S processor line (5)
Transactional Synchronization Extension (TSX)
Intel’s TSX is basically an ISA extension and its implementation to allow hardware supported
transactional memory.
Transactional memory is an efficient synchronization mechanism in concurrent programming
used to effectively manage race conditions occurring when multiple threads access shared
data.

## Slide 124: 3.4 The Haswell-EX (E7-4800 v3) 4S processor line (6)
Addressing race conditions
Basically there are two mechanisms to address race conditions in multithreaded programs,
as indicated below:
Locks
Transactional memory (TM)
Basic mechanisms to address races in multithreaded programs
Pessimistic approach,
it intends to prevent possible conflicts
by enforcing serialization of transactions
through locks.
Optimistic approach,
it allows parallel execution and thus
lets access conflicts to occur
but provides a checking and repair mechanism
for managing these conflicts, i.e.
it allows all threads to access shared data simultaneously
but after completing a transaction,
it will be checked whether a conflict arose,
if yes, the transaction will be rolled back and
then replayed if feasible else
executed while using locks.
The next Figure illustrates these synchronization mechanisms.

## Slide 125: 3.4 The Haswell-EX (E7-4800 v3) 4S processor line (7)
Illustration of lock based and transaction memory (TM) based thread synchronization
[126]
Conflict, to be
repaired

## Slide 126: 3.4 The Haswell-EX (E7-4800 v3) 4S processor line (8)
We note that in their POWER8 (2014) IBM also introduced hardware supported transactional
memory, called Hardware Transactional Memory (HTM).

## Slide 127: 3.4 The Haswell-EX (E7-4800 v3) 4S processor line (9)
Contrasting the layout of the Haswell-EX cores vs. the Ivy Bridge-EX cores [111]
Haswell-EX has four core slides with 3x4 + 6 = 18 cores rather than 3x5 cores in case of
the Ivy Bridge-EX (only 3x 4 = 12 cores indicated in the Figure below).
Figure: Contrasting the basic layout of the Haswell-EX (E7 v3) and Ivy Bridge-EX (E7 v2)
processors [111]
Note that the E7-V3 has only two ring buses interconnected by a pair of buffered switches.

## Slide 128: 3.4 The Haswell-EX (E7-4800 v3) 4S processor line (10)
More detailed layout of the Haswell-EX die [111]

## Slide 129: 3.4 The Haswell-EX (E7-4800 v3) 4S processor line (11)
Die micrograph of an 18-core Haswell-EX processor [111]
22 nm, 5.7 billion transistors, 662 mm2

## Slide 130: 3.4 The Haswell-EX (E7-4800 v3) 4S processor line (12)
Main features of 4S and 8S Haswell-EX processors [120]

## Slide 131: 3.4 The Haswell-EX (E7-4800 v3) 4S processor line (13)
P4-based Tulsa (2006)
Performance comparison of MP processors -1 [121]
(The test workload is: CPU 45 nm Design Rule Check Tool C 2006 Rev.)
Core 2 Tigerton QC (2007)
Penryn Dunnington (2008)
Nehalem-EX (2010)
Westmere-EX (2011)
Ivy Bridge-EX (2014)
Haswell-EX (2015)

## Slide 132: 3.4 The Haswell-EX (E7-4800 v3) 4S processor line (14)
Performance comparison of MP processors -2 [121]
Note that with their MP line Intel achieved a more than 10-fold performance boost in 10 years.

## Slide 133
3.5 The Broadwell-EX (E7-4800 v4) 4S processor line
Notes: 133

## Slide 134: 3.5 The Broadwell-EX (E7-4800 v4) 4S processor line (1)
3.5 The Broadwell-EX (E7-4800 v4) 4S processor line
Positioning the Broadwell-EX line [112]

## Slide 135: 3.5 The Broadwell-EX (E7-4800 v4) 4S processor line (2)
Planned features of the Brickland platform with the Broadwell-EX processor line -1 [122]

## Slide 136: 3.5 The Broadwell-EX (E7-4800 v4) 4S processor line (3)
Planned features of the Broadwell-EX processor line -2 [122]
As seen in the above Table, the planned features – except of having 24 cores – are the same
as implemented in the Haswell-EX line.

## Slide 137
4. Example 2: The Purley platform
Notes: 137

## Slide 138: 4. Example 2:. The Purley platform (1)
4. Example 2: The Purley platform
According to leaked Intel sources it is planned to be introduced in 2017.
It is based on the 14 nm Skylake family.

## Slide 139: 4. Example 2:. The Purley platform (2)
Positioning of the Purley platform [112]

## Slide 140: 4. Example 2:. The Purley platform (3)
Planned features of the Purley platform with the Skylake-EX processor line -1 [122]

## Slide 141: 4. Example 2:. The Purley platform (4)
Key advancements of the Purley platform [123]

## Slide 142: 4. Example 2:. The Purley platform (5)
Example of a 2S Purley platform [123]
10GBASE-T: 10 Gbit/s Ethernet via copper twisted pair cable
(Lewisburg)

## Slide 143
5. References
Notes: 143

## Slide 144: 5. References (1)
[1]: Radhakrisnan S., Sundaram C. and Cheng K., „The Blackford Northbridge Chipset for the
Intel 5000”, IEEE Micro, March/April 2007, pp. 22-33
[2]: Next-Generation AMD Opteron Processor with Direct Connect Architecture – 4P Server
Comparison, http://www.amd.com/us-en/assets/content_type/DownloadableAssets/4P_
Server_Comparison_PID_41461.pdf
[3]: Intel® 5000P/5000V/5000Z Chipset Memory Controller Hub (MCH) – Datasheet,
Sept. 2006. http://www.intel.com/design/chipsets/datashts/313071.htm
[4]: Intel® E8501 Chipset North Bridge (NB) Datasheet, Mai 2006,
http://www.intel.com/design/chipsets/e8501/datashts/309620.htm
[5]: Conway P & Hughes B., „The AMD Opteron Northbridge Architecture”, IEEE
MICRO, March/April 2007, pp. 10-21
[6]: Intel® 7300 Chipset Memory Controller Hub (MCH) – Datasheet, Sept. 2007,
http://www.intel.com/design/chipsets/datashts/313082.htm
[7]: Supermicro Motherboards, http://www.supermicro.com/products/motherboard/
[8]: Sander B., „AMD Microprocessor Technologies,” 2006,
http://www.ewh.ieee.org/r4/chicago/foxvalley/IEEE_AMD_Meeting.ppt
[9]: AMD Quad FX Platform with Dual Socket Direct Connect (DSDC) Architecture,
http://www.asisupport.com/ts_amd_quad_fx.htm
[10]: Asustek motherboards - http://www.asus.com.tw/products.aspx?l1=9&l2=39
http://support.asus.com/download/model_list.aspx?product=5&SLanguage=en-us

## Slide 145: 5. References (2)
[11]: Kanter, D. „A Preview of Intel's Bensley Platform (Part I),” Real Word Technologies,
Aug. 2005, http://www.realworldtech.com/page.cfm?ArticleID=RWT110805135916&p=2
[12]: Kanter, D. „A Preview of Intel's Bensley Platform (Part II),” Real Word Technologies,
Nov. 2005, http://www.realworldtech.com/page.cfm?ArticleID=RWT112905011743&p=7
[13]: Quad-Core Intel® Xeon® Processor 7300 Series Product Brief, Intel, Nov. 2007
http://download.intel.com/products/processor/xeon/7300_prodbrief.pdf
[14]: „AMD Shows Off More Quad-Core Server Processors Benchmark” X-bit labs, Nov. 2007
http://www.xbitlabs.com/news/cpu/display/20070702235635.html
[15]: AMD, Nov. 2006 http://www.asisupport.com/ts_amd_quad_fx.htm
[16]: Rusu S., “A Dual-Core Multi-Threaded Xeon Processor with 16 MB L3 Cache,” Intel, 2006,
http://ewh.ieee.org/r5/denver/sscs/Presentations/2006_04_Rusu.pdf
[17]: Goto H., Intel Processors, PCWatch, March 04 2005,
http://pc.watch.impress.co.jp/docs/2005/0304/kaigai162.htm
[18]: Gilbert J. D., Hunt S., Gunadi D., Srinivas G., “The Tulsa Processor,” Hot Chips 18, 2006,
http://www.hotchips.org/archives/hc18/3_Tues/HC18.S9/HC18.S9T1.pdf
[19]: Goto H., IDF 2007 Spring, PC Watch, April 26 2007,
http://pc.watch.impress.co.jp/docs/2007/0426/hot481.htm

## Slide 146: 5. References (3)
[20]: Hruska J., “Details slip on upcoming Intel Dunnington six-core processor,” Ars technica,
February 26, 2008, http://arstechnica.com/news.ars/post/20080226-details-slip-on-
upcoming-intel-dunnington-six-core-processor.html
[21]: Goto H., 32 nm Westmere arrives in 2009-2010, PC Watch, March 26 2008,
http://pc.watch.impress.co.jp/docs/2008/0326/kaigai428.htm
[22]: Singhal R., “Next Generation Intel Microarchitecture (Nehalem) Family:
Architecture Insight and Power Management, IDF Taipeh, Oct. 2008,
http://intel.wingateweb.com/taiwan08/published/sessions/TPTS001/FA08%20IDF
-Taipei_TPTS001_100.pdf
[23]: Smith S. L., “45 nm Product Press Briefing,”, IDF Fall 2007,
ftp://download.intel.com/pressroom/kits/events/idffall_2007/BriefingSmith45nm.pdf
[24]: Bryant D., “Intel Hitting on All Cylinders,” UBS Conf., Nov. 2007,
http://files.shareholder.com/downloads/INTC/0x0x191011/e2b3bcc5-0a37-4d06-
aa5a-0c46e8a1a76d/UBSConfNov2007Bryant.pdf
[25]: Barcelona's Innovative Architecture Is Driven by a New Shared Cache,
http://developer.amd.com/documentation/articles/pages/8142007173.aspx
[26]: Larger L3 cache in Shanghai, Nov. 13 2008, AMD,
http://forums.amd.com/devblog/blogpost.cfm?threadid=103010&catid=271
[27]: Shimpi A. L., “Barcelona Architecture: AMD on the Counterattack,” March 1 2007,
Anandtech, http://www.anandtech.com/cpuchipsets/showdoc.aspx?i=2939&p=1

## Slide 147: 5. References (4)
[28]: Rivas M., “Roadmap update,”, 2007 Financial Analyst Day, Dec. 2007, AMD,
http://download.amd.com/Corporate/MarioRivasDec2007AMDAnalystDay.pdf
[29]: Scansen D., “Under the Hood: AMD’s Shanghai marks move to 45 nm node,”
EE Times, Nov. 11 2008,
http://www.eetimes.com/news/latest/showArticle.jhtml?articleID=212002243
[30]: 2-way Intel Dempsey/Woodcrest CPU Bensley Server Platform, Tyan,
http://www.tyan.com/tempest/training/s5370.pdf
[31]: Gelsinger P. P., “Intel Architecture Press Briefing,”, 17. March 2008,
http://download.intel.com/pressroom/archive/reference/Gelsinger_briefing_0308.pdf
[32]: Mueller S., Soper M. E., Sosinsky B., Server Chipsets, Jun 12, 2006,
http://www.informit.com/articles/article.aspx?p=481869
[33]: Goto H., IDF, Aug. 26 2005,
http://pc.watch.impress.co.jp/docs/2005/0826/kaigai207.htm
[34]: TechChannel, http://www.tecchannel.de/_misc/img/detail1000.cfm?pk=342850&
fk=432919&id=il-74145482909021379
[35]: Intel quadcore Xeon 5300 review, Nov. 13 2006, Hardware.Info,
http://www.hardware.info/en-US/articles/amdnY2ppZGWa/Intel_quadcore_Xeon_
5300_review
[36]: Wasson S., Intel's Woodcrest processor previewed, The Bensley server platform debuts,
Mai 23, 2006, The Tech Report, http://techreport.com/articles.x/10021/1

## Slide 148: 5. References (5)
[37]: Enderle R., AMD Shanghai “We are back! TGDaily, November 13, 2008,
http://www.tgdaily.com/content/view/40176/128/
[38]: Clark J. & Whitehead R., “AMD Shanghai Launch, Anandtech, Nov. 13 2008,
http://www.anandtech.com/showdoc.aspx?i=3456
[39]: Chiappetta M., AMD Barcelona Architecture Launch: Native Quad-Core, Hothardware,
Sept. 10, 2007,
http://hothardware.com/Articles/AMD_Barcelona_Architecture_Launch_Native_
QuadCore/
[40]: Hachman M., “AMD Phenom, Barcelona Chips Hit By Lock-up Bug,”, ExtremeTech,
Dec. 5 2007, http://www.extremetech.com/article2/0,2845,2228878,00.asp
[41]: AMD Opteron™ Processor for Servers and Workstations, http://amd.com.cn/CHCN/Processors/ProductInformation/0,,30_118_8826_8832,
00-1.html
[42]: AMD Opteron Processor with Direct Connect Architecture, 2P Server Power Savings
Comparison, AMD,
http://enterprise.amd.com/downloads/2P_Power_PID_41497.pdf
[43]: AMD Opteron Processor with Direct Connect Architecture, 4P Server Power Savings
Comparison, AMD,
http://enterprise.amd.com/downloads/4P_Power_PID_41498.pdf
[44]: AMD Opteron Product Data Sheet, AMD,
http://pdfs.icecat.biz/pdf/1868812-2278.pdf

## Slide 149: 5. References (6)
[45]: Images, Xtreview,
http://xtreview.com/images/K10%20processor%2045nm%20architec%203.jpg
[46]: Kanter D., “Inside Barcelona: AMD's Next Generation, Real World Tech., Mai 16 2007,
http://www.realworldtech.com/page.cfm?ArticleID=RWT051607033728
[47]: Kanter D,, “AMD's K8L and 4x4 Preview, Real World Tech. June 02 2006,
http://www.realworldtech.com/page.cfm?ArticleID=RWT060206035626&p=1
[48]: Kottapali S., Baxter J., “Nehalem-EX CPU Architecture”, Hot Chips 21, 2009,
http://www.hotchips.org/archives/hc21/2_mon/HC21.24.100.ServerSystemsI-Epub/
HC21.24.122-Kottapalli-Intel-NHM-EX.pdf
[49]: Kahn O., Piazza T., Valentine B., “Technology Insight: Intel next Generation
Microarchitecture Codename Sandy Bridge, IDF, San Francisco, Sept. 2010
[50]: Piazza T., Jiang H., “Intel Next Generation Microarchitecture Codename Sandy Bridge:
Processor Graphics, IDF, San Francisco, Sept. 2010
[51]: Braun-Protte T., “Intel die neuste Generation”, March 2010,
https://sp.ts.fujitsu.com/dmsp/docs/02_fujitsu_intel_server_cpu.pdf
[52]: De Gelas J., The Intel Xeon E7-8800 v3 Review: The POWER8 Killer?, AnandTech,
May 8 2015, http://www.anandtech.com/show/9193/the-xeon-e78800-v3-review
[53]: Tyan Confidential, Tempest i5000VF S5370, 2-way Intel Dempsey/Woodcrest CPU
Bensley Server Platform, http://www.tyan.com/tempest/training/s5370.pdf

## Slide 150: 5. References (7)
[55]: Neiger G., Santoni A., Leung F., Rodgers D., Uhlig R., Intel® Virtualization Technology:
Hardware support for efficient processor virtualization, Aug. 10 2006, Vol. 10, Issue 3,
http://www.intel.com/technology/itj/2006/v10i3/1-hardware/1-abstract.htm
[56]: Intel Software Networks: Forums,
http://software.intel.com/en-us/forums/showthread.php?t=56802
[57]: Wikipedia: x86 virtualization, 2011,
http://en.wikipedia.org/wiki/X86_virtualization#Intel_virtualization_.28VT-x.29
[54]: Intel 5520 Chipset and Intel 5500 Chipset, Datasheet, March 2009,
http://www.intel.com/content/www/us/en/chipsets/5520-5500-chipset-ioh-datasheet.html
[58]: Sharma D. D., Intel 5520 Chipset: An I/O Hub Chipset for Server, Workstation, and High
End Desktop, Hotchips 2009, http://www.hotchips.org/archives/hc21/2_mon/
HC21.24.200.I-O-Epub/HC21.24.230.DasSharma-Intel-5520-Chipset.pdf
[59]: Morgan T. P., Intel's future Sandy Bridge Xeons exposed, May 30 2011, The Register,
http://www.theregister.co.uk/2011/05/30/intel_sandy_bridge_xeon_platforms/page2.html
[60]: Gilbert J. D., Hunt S. H., Gunadi D., Srinivas G., The Tulsa Processor: A Dual Core Large
Shared-Cache Intel Xeon Processor 7000 Sequence for the MP Server Market Segment,
Aug 21 2006, http://www.hotchips.org/archives/hc18/3_Tues/HC18.S9/HC18.S9T1.pdf
[61]: Intel Server Board Set SE8500HW4, Technical Product Specification, Revision 1.0,
May 2005, ftp://download.intel.com/support/motherboards/server/sb/se8500hw4_board
_set_tpsr10.pdf

## Slide 151: 5. References (8)
[62]: Mitchell D., Intel Nehalem-EX review, PCPro,
http://www.pcpro.co.uk/reviews/processors/357709/intel-nehalem-ex
[64]: Intel Xeon Processor E7-8800/4800/2800 Product Families, Datasheet Vol. 1 of 2,
April 2011, http://www.intel.com/Assets/PDF/datasheet/325119.pdf
[63]: Nagaraj D., Kottapalli S.: Westmere-EX: A 20 thread server CPU, Hot Chips 2010
http://www.hotchips.org/uploads/archive22/HC22.24.610-Nagara-Intel-6-Westmere-EX.pdf
[65]: Supermicro P4QH6 / P4QH8 User’s Manual, 2002,
http://www.supermicro.com/manuals/motherboard/GC-HE/MNL-0665.pdf
[66]: Intel Xeon Processor 7500/6500 Series, Public Gold Presentation, March 30 2010,
http://cache-www.intel.com/cd/00/00/44/64/446456_446456.pdf
[67]: Supermicro X8QB6-F / X8QBE-F User’s Manual, 2010,
http://files.siliconmechanics.com/Documentation/Rackform/iServ/R413/Mainboard/MNL
-X8QB-E-6-F.pdf
[68]: Rusu & al.: A 45 nm 8-Core Enterprise Xeon Processor, IEEE journal of Solid State Circuits,
Vol. 45, No. 1, Jan. 2010, pp. 7-14
[69]: Jafarjead B., “Intel Core Duo Processor,” Intel, 2006,
http://masih0111.persiangig.com/document/peresentation/behrooz%20jafarnejad.ppt
[70]: Keutzer K., Malik S., Newton R., Rabaey J., Sangiovanni-Vincentelli A., System Level Design:
Orthogonalization of Concerns and Platform-Based Design, IEEE Transactions on
Computer-Aided Design of Circuits and Systems, Vol. 19, No. 12, Dec. 2000, pp.?????

## Slide 152: 5. References (9)
[71]: Perich D., Intel Volume platforms Technology Leadership, Presentation at HP World 2004,
http://98.190.245.141:8080/Proceed/HPW04CD/papers/4194.pdf
[72]: Krazit T., Intel Sheds Light on 2005 Desktop Strategy, IDG News Service, Dec. 07 2004,
http://pcworld.about.net/news/Dec072004id118866.htm
[73]: Molka D., Hackenberg D., Schöne R., Müller M. S., Memory Performance and Cache
Coherency Effects on an Intel Nehalem multiprocessor System, Proc. 18th Int. Conf.
on Parallel Architectures and Compilation, Techniques, PACT 2009,
http://doi.ieeecomputersociety.org/10.1109/PACT.2009.22
[74]: Radhakrishnan S., Chinthamani S., Cheng K., The Blackford Northbridge Chipset for
Intel 5000, IEEE MICRO, March-April 2007, pp. 22-33
[75]: Rolf T., Cache Organization and Memory Management of the Intel Nehalem Computer
Architecture, University of Utah, Dec. 2009, http://rolfed.com/nehalem/nehalemPaper.pdf
[76]: Levinthal D., Performance Analysis Guide for Intel Core i7 Processor and Intel Xeon 5500
processors, Version 1.0, 2008
http://software.intel.com/sites/products/collateral/hpc/vtune/performance_analysis_
guide.pdf
[79]: Gavrichenkov I., Workstation Processors Duel: AMD Opteron against Intel Xeon, Page 5
12/21/2005,
http://www.xbitlabs.com/articles/cpu/display/opteron-xeon-workstation_5.html
[78]: 3.6GHz 2MB 800MHz Intel Xeon Processor SL7ZC C8511, http://store.flagshiptech.com/
products/3.6GHz-2MB-800MHz-Intel-Xeon-Processor-SL7ZC-C8511.html
[77]: Ryszard Sommefeldt R., Intel Xeon 3.4GHz ['Nocona' core], 18th Aug, 2004, http://www.hexus.net/content/item.php?item=822&page=1&search=reas

## Slide 153: 5. References (10)
[80]: Glaskowsky P.: Investigating Intel's Lynnfield mysteries, cnet News, Sept. 21. 2009,
http://news.cnet.com/8301-13512_3-10357328-23.html
[81]: Kurd & al., Westmere: A Family of 32 nm IA Processors, Proc. ISSCC 2010, pp. 96-98
[82]: Miller M. J.,Intel Previews ISSCC: 6-Core Gulftown Processor, Feb 03, 2010, http://
forwardthinking.pcmag.com/chips/282694-intel-previews-isscc-6-core-gulftown-processor
[83]: Hill D., Chowdhury M., Westmere Xeon-56xx “Tick” CPU, Hot Chips 22, 2010,
http://www.hotchips.org/uploads/archive22/HC22.24.620-Hill-Intel-WSM-EP-print.pdf
[84]: Pawlowski S.: Intelligent and Expandable High- End Intel Server Platform, Codenamed
Nehalem-EX, IDF 2009
[85]: Intel Sandy Bridge Review, Bit-tech, Jan. 3 2011,
http://www.bit-tech.net/hardware/cpus/2011/01/03/intel-sandy-bridge-review/1
[86]: Kahn O., Piazza T., Valentine B.: Technology Insight: Intel Next Generation
Microarchitecture Codename Sandy Bridge, IDF 2010
extreme.pcgameshardware.de/.../281270d1288260884-bonusmaterial-pc- games-
ardware-12-2010-sf10_spcs001_100.pdf
[87]: Inkley B., Tetrick S., Intel Multi-core Architecture and Implementations, IDF, Session
MATS002, March 7 2006
[88]: Smith S. L., Intel Roadmap Overview, IDF Fall, Aug. 20 2008
http://download.intel.com/pressroom/kits/events/idffall_2008/SSmith_briefing_roadmap.pdf
[89]: Intel Public Roadmap; Business Platforms for Desktop, Mobile & Data Center, H1’ 2011
http://www.2ncinesil.com/download/Public%20Roadmap%201H%202011.pptx

## Slide 154: 5. References (11)
[90]: Rusu S., „Circuit Technologies for Multi-Core Processor Design,” April 2006,
http://www.ewh.ieee.org/r6/scv/ssc/April06.pdf
[91]: Goto H., IDF, Aug. 26 2005,
http://pc.watch.impress.co.jp/docs/2005/0826/kaigai207.htm
[92]: TechChannel, http://www.tecchannel.de/_misc/img/detail1000.cfm?pk=342850&
fk=432919&id=il-74145482909021379
[94]: Morgan T. P., Intel's future Sandy Bridge Xeons exposed, The Register, May 30. 2011,
http://www.theregister.co.uk/2011/05/30/intel_sandy_bridge_xeon_platforms
[95]: Gelsinger P., Keynote, IDF Spring 2005, March 2005,
http://www.intel.com/pressroom/kits/events/idfspr_2005/index.htm
[93]: Sandy Bridge, http://en.wikipedia.org/wiki/Sandy_Bridge
[96]: Kuppuswamy, R. C al., Over one million TPCC with a 45nm 6-core Xeon® CPU,
IEEE International Solid-State Circuits Conference - Digest of Technical Papers,
ISSCC 2009, Feb. 2009, pp. 70 - 71,71a
[97]: Perich D., Intel Volume Platforms Technology Leadership, Solutions and Technology
Conference, HP World 2004,
http://www.openmpe.com/cslproceed/HPW04CD/papers/4194.pdf
[98]: De Gelas J., Westmere-EX: Intel Improves their Xeon Flagship, AnandTech, April 6 2011,
http://www.anandtech.com/show/4259/westmereex-intels-flagship-improves
[99]: Starke W.J., POWER7: IBM’s Next Generation, Balanced POWER Server Chip, Hot Chips 21,
http://www.hotchips.org/wp-content/uploads/hc_archives/hc21/3_tues/HC21.25.800.
ServerSystemsII-Epub/HC21.25.835.Starke-IBM-POWER7SystemBalancev13_display.pdf

## Slide 155: 5. References (12)
[101]: Intel Server System SSH4 Board Set, Technical Product Specification, Oct. 2003,
http://download.intel.com/support/motherboards/server/ssh4/ssh4_tps.pdf
[102]: Haas J. & Vogt P., Fully buffered DIMM Technology Moves Enterprise Platforms to the
Next Level, Technology Intel Magazine, March 2005, pp. 1-7
[103]: Ganesh B., Jaleel A., Wang D., Jacob B., Fully-Buffered DIMM Memory Architectures:
Understanding Mechanisms, Overheads and Scaling, 2007,
https://ece.umd.edu/~blj/papers/hpca2007.pdf
[100]: Intel E8500 Chipset eXternal Memory Bridge (XMB), Datasheet, March 2005,
http://www.intel.co.id/content/dam/doc/datasheet/e8500-chipset-external-memory-
bridge-datasheet.pdf
[104]: Smith S. L., Quad-Core Press Briefing, IDF 2006,
http://www.intel.com/pressroom/kits/quadcore/qc_pressbriefing.pdf
[105]: Smith S.L., Intel Enterprise Roadmap, IDF 2010
[106]: Intel 7500 Chipset, Datasheet, March 2010,
http://www.intel.com/content/dam/doc/datasheet/7500-chipset-datasheet.pdf
[107]: 7500/7510/7512 Scalable Memory Buffer, Datasheet, April 2011,
http://www.intel.com/content/www/us/en/chipsets/7500-7510-7512-scalable-memory-
buffer-datasheet.html
[108]: X8QB6-LF User Manual, Supermicro

## Slide 156: 5. References (13)
[110]: Morgan T. P., Intel (finally) uncages Nehalem-EX beast, The Register, March 30 2010,
http://www.theregister.co.uk/2010/03/30/intel_nehalem_ex_launch/?page=2
[111]: Morgan T. P., Intel Puts More Compute Behind Xeon E7 Big Memory, The Platform,
May 5 2015, http://www.theplatform.net/2015/05/05/intel-puts-more-compute-behind-
xeon-e7-big-memory/
[112]: Niederste-Berg M., 28 core Skylake EP/EX plattform comes into view, Hardware LUXX,
26 May 2015, http://www.hardwareluxx.com/index.php/news/hardware/cpu/35474-
28-core-skylake-epex-plattform-comes-into-view.html
[109]: Baseboard management controller (BMC) definition, TechTarget, May 2007,
http://searchnetworking.techtarget.com/definition/baseboard-management-controller
[113]: Intel C102/C104 Scalable Memory Buffer, Datasheet, Febr. 2014,
http://www.intel.com/content/dam/www/public/us/en/documents/datasheets/c102-c104-
scalable-memory-buffer-datasheet.pdf
[114]: Intel Xeon Processor E7-8800/4800 V3 Product Family, Technical Overview, May 21 2015,
https://software.intel.com/en-us/articles/intel-xeon-processor-e7-88004800-v3-product-
family-technical-overview
[115]: X10QBi Platform with X10QBi Baseboard, User’s manual, Supermicro, 2014,
ftp://ftp.supermicro.com/CDR-X10-Q_1.00_for_Intel_X10_Q_platform/MANUALS/X10QBi.pdf
[116]: Rusu S., Muljono H., Ayers D., Tam S., A 22nm 15-core enterprise Xeon processor family,
IEEE ISSC Journal, Vol. 50, Issue 1, Jan. 2015

## Slide 157: 5. References (14)
[118]: Chiappetta M., Intel Launches Xeon E7-8800 and E7-4800 v3 Processor Families,
Hot Hardware, May 5 2015,
http://hothardware.com/reviews/intel-launches-xeon-e7-v3-family-of-processors
[119]: Broadwell-EX/EP disappear from the latest Intel roadmap, AnandTech Forums,
http://forums.anandtech.com/showthread.php?t=2439161
[117]: Esmer I., Ivybridge Server Architecture: A Converged Server, Aug. 2014, Hot Chips 2014,
http://www.hotchips.org/wp-content/uploads/hc_archives/hc26/HC26-12-day2-epub/
HC26.12-8-Big-Iron-Servers-epub/HC26.13.832-IvyBridge-Esmer-Intel-IVB%20Server%
20Hotchips2014.pdf
[120]: Accelerate Big Data Insights with the Intel Xeon Processor E7-8800/4800 v3 Product
Families, Product Brief, 2015,
http://www.intel.com/newsroom/kits/xeon/e7v3/pdfs/Xeon_E7v3_ProductBrief.pdf
[121]: Accelerating Silicon Design with the Intel Xeon Processor E7-8800 v3 Product Family, 2015,
http://www.intel.com/content/dam/www/public/us/en/documents/product-briefs/xeon-
processor-e7-8800-v3-brief.pdf
[122]: Broadwell-EX/EP disappeared from Intel's enterprise roadmaps, Linus Tech Tips,
July 16 2015, http://linustechtips.com/main/topic/409185-broadwell-exep-disappeared-
from-intels-enterprise-roadmaps/
[123]: van Monsjou D., Massive Leak shows details on Skylake Xeon Chips, Overclock3D,
May 25 2015, http://www.overclock3d.net/articles/cpu_mainboard/massive_leak_shows_
details_on_skylake_xeon_chips/1

## Slide 158: 5. References (15)
[124]: Server duel: Xeon Woodcrest vs. Opteron Socket F, Tweakers, 7 September 2006,
http://tweakers.net/reviews/646/2/server-duel-xeon-woodcrest-vs-opteron-socket-f-
post-mortem-netburst.html
[125]: Papazian I. E. & al., Ivy Bridge Server: A Converged Design, IEEE MICRO, March-April
2015, pp. 16-25,
http://ieeexplore.ieee.org/xpl/articleDetails.jsp?reload=true&arnumber=7091791
[126]: Gao Y., HPC Workload Performance Tuning on POWER8 with IBM XL Compilers and Libraries,
SPXXL/Scicomp Summer Workshop 2014, http://spscicomp.org/wordpress/wp-content/
uploads/2014/05/gao-IBM-XL-compilers-for-POWER8-Scicomp-2014.pdf
[127]: New Xeon Processor Numbering, More Than Just a Number, Intel.com, April 5 2011,
https://communities.intel.com/community/itpeernetwork/datastack/blog/2011/04/05/
new-xeon-processor-numbering-more-than-just-a-number
[128]: Gwennap L., ThunderX rattles server market, Microprocessor Report, June 9, 2014,
http://www.cavium.com/pdfFiles/ThunderX_Rattles_Server_Market.pdf
[129]: TN-47-21: FBDIMM - Channel Utilization, Micron, 12/2009,
https://www.micron.com/resource-details/2bedbfb2-1573-447b-a779-9838be9a131d
[130]: De Gelas, The Intel Xeon D Review: Performance Per Watt Server SoC Cfhampion?
Anandtech, June 23 2015,
http://www.anandtech.com/show/9185/intel-xeon-d-review-performance-per-watt-
server-soc-champion

## Slide 159
Processor
MCH
ICH
FSB
Processor
E.g. DDR2-533
ESI
E.g. DDR3-1333
Processor
IOH1
QPI
QPI
ICH
ESI
QPI
E.g. DDR3-1333
Processor
1ICH: I/O hub
ESI: Enterprise
System Interface
Connect memory
distributed via the processors
Connect memory
globally via an interconnect
Connecting memory to the processors
Connect memory
centrally via the MCH
(Memory Control Hub)
Processor
Processor
GPU
Interconnect
MC
MC
IO
IO
The central connection of memory
causes severe bandwidth imitations
first of all for MP configurations.
Per processor connected memory
provides inherent scaling
of the memory bandwidth
with the processor count.
An interconnect provides
the interconnection for all
system components
Main alternartives for connecting memory to a platform