## Slide 1
Sima Dezső
2015 October
(Ver. 2.2)
 Sima Dezső, 2015
The mobile boom

## Slide 2
2. The smartphone boom
Contents
1. The traditional computer market
4. Requirements of mobile devices
6. Conclusions
7. References
3. The tablet boom
5. How leading IT vendors addressed the mobile boom?

## Slide 3
1. The traditional computer market
Notes: 3

## Slide 4: 1. The traditional computer market (1)
1. The traditional computer market
Desktops
Embedded
computer devices
Main computer market segments around 2000
Intel’s Pentium 4 lines
AMD’s Athlon lines
ARM’s lines
Servers
Intel’s Xeon lines
AMD’s Opteron lines
E.g.
Major trend in the first half of the 2000’s: spreading of laptops (first mobile devices)

## Slide 5: 1. The traditional computer market (2)
Intel’s Pentium 4 lines
AMD’s Athlon64 lines
ARM’s lines
Intel’s Xeon lines
AMD’s Opteron lines
E.g.
Desktops
Embedded
computer devices
Main computer market segments around 2005
Servers
Laptops
Intel’s Celeron lines
AMD’s Duron lines

## Slide 6: 1. The traditional computer market (4)
Server market revenues by vendor ($US Billion) – 2003-2012 [14]
≈75 %
≈18 %
≈ 7 %
Intel/AMD
IBM POWER/Sun etc.
IBM

## Slide 7: 1. The traditional computer market (5)
x86 server market share of Intel and AMD [17]
Core 2 Quad DP
Penryn DP
Penryn MP
Nehalem-EX DP/MP
Core 2 DP
K10 Barcelona MP
K10 Shanghai MP
K10 Magny Course MP
K10 Istambul MP
Source: IDC,
Mercury Research

## Slide 8: 1. The traditional computer market (6)
Worldwide market share of x86 and RISC 4S/4S+ servers (by volume) [51]
MSS: Market Segment Share
Source: IDC World Wide Server Tracker Q4’14

## Slide 9: 1. The traditional computer market (7)
Worldwide PC shipments by quarter, Q2 1999 – Q2 2013 [18]

## Slide 10: 1. The traditional computer market (8)
Worldwide PC shipments by quarter Q1 2009 – Q2 2015 by vendor [52]

## Slide 11
2. Emergence and spread of smartphones
Notes: 11

## Slide 12: 2. Emergence and spread of smartphones (1)
Diversification of mobile devices mainly after 2005 [2]
The mobile boom
2. Emergence and spread of smartphones

## Slide 13: 2. Emergence and spread of smartphones (2)
Emergence of smartphones-1
Forerunners of smartphones emerged already
at the beginning of the 2000’s, like Nokia’s 7650
(shipped in 2002).
Figure: Nokia’s 7650 [39]
The 7650 became the first widely available phone
with camera and color screen but supported
no video.
It was the first Nokia phone running under
the Symbian OS.

## Slide 14: 2. Emergence and spread of smartphones (3)
The emergence of smartphones is often
contributed to the BlackBerry Pearl 8100
line of the Canadian firm RIM
(Research in Motion)[5].
This phone – shipped in 2006 - supported
beyond a camera also video and became
very popular in the US.
It was run under the BlackBerry OS.
Emergence of smartphones-2
Figure: RIM’s BlackBarry Perl 8100
(2006) [38]

## Slide 15: 2. Emergence and spread of smartphones (4)
Early spread of smartphones-1
In 2007 Apple’s iPhone gave a strong momentum for rapid spreading of
smartphones.
It run under the iPhone OS (renamed later to iOS in 2010).
Figure: Steve Jobs introducing the iPhone at MacWorld Expo in 1/2007 [47]

## Slide 16: 2. Emergence and spread of smartphones (7)
Worldwide unit shipments of PCs vs. smartphones 2005-2013 [37]
PCs: Desktop PCs + notebook PCs

## Slide 17: 2. Emergence and spread of smartphones (8)
Worldwide unit shipment estimates of PCs vs. smartphones 2011-2017 [28]
Source: Gartner

## Slide 18: 2. Emergence and spread of smartphones (9)
Company | 2Q15 Units | 2Q15 Market Share (%) | 2Q14 Units | 2Q14 Market Share (%)
Samsung | 72,072.5 | 21.9 | 76,129.2 | 26.2
Apple | 48,085.5 | 14.6 | 35,345.3 | 12.2
Huawei | 25,825.8 | 7.8 | 17,657.7 | 6.1
Lenovo* | 16,405.9 | 5.0 | 19,081.2 | 6.6
Xiaomi | 16,064.9 | 4.9 | 12,540.8 | 4.3
Others | 151,221.7 | 45.9 | 129,630.2 | 44.6
Total | 329,676.4 | 100.0 | 290,384.4 | 100.0
Table 1
Worldwide Smartphone Sales to End Users by Vendor in 2Q15 (Thousands of Units)
Source: Gartner (August 2015)
Worldwide smartphone sales to end user by vendor in 2Q 2015 [53]
(Thousands of units)

## Slide 19: 2. Emergence and spread of smartphones (10)
Worldwide market share of smartphone OSs in 2009 [41]
Nokia
RIM
(BlackBerry)
Apple
MS
Google

## Slide 20: 2. Emergence and spread of smartphones (11)
Worldwide market share of smartphone OSs in 2012-2014 [42]

## Slide 21: 2. Emergence and spread of smartphones (12)
Operating System | 2Q15 Units | 2Q15 Market Share (%) | 2Q14 Units | 2Q14 Market Share (%)
Android | 271,010 | 82.2 | 243,484 | 83.8
iOS | 48,086 | 14.6 | 35,345 | 12.2
Windows | 8,198 | 2.5 | 8,095 | 2.8
BlackBerry | 1,153 | 0.3 | 2,044 | 0.7
Others | 1,229.0 | 0.4 | 1,416.8 | 0.5
Total | 329,676.4 | 100.0 | 290,384.4 | 100.0
Worldwide Smartphone Sales to End Users by Operating System in 2Q15 (Thousands of Units)
Source: Gartner (August 2015)
Worldwide smartphone sales to end user by OS in 2Q 2015 [53]
(Thousands of units)

## Slide 22: 2. Emergence and spread of smartphones (13)
Worldwide market share of application processors in Q1 2014 used in
smartphones (based on revenue) [43]
Vendor | Market share | Processor line | Core | ISA
Qualcomm (USA) | 53 % | Snapdragon 200-800 | Qualcomm designed Krait cores ARM Cortex A line | ARMv7 ARMv7/v8
Apple (USA) | 16 % | Apple A6 Apple A7 | ARM Cortex A8 Apple designed Cyclone core | ARMv7 ARMv8
MediaTek (Taiwan) | 13 % | MT6595 MT67xx | 4xARM Cortex A7/ 4xA17 (ARM big.LITTLE) 4xARM Cortex A53/4x A57 (ARM big.LITTLE) | ARMv7 ARMv8
Samsung (S. Korea) |  | Exynos | ARM Cortex A line | ARMv7 ARM v8
Spreadtrum (China) |  | SC77xx/88xx | ARM Cortex A5/A7 | ARMv7

## Slide 23: 2. Emergence and spread of smartphones (14)
Model | Released | Technology | CPU | Word length bit | Clock rate (up to) | Connectivity
820 | 2016 | 14 nm FinFET | Kryo 2.2 GHz (DC) + Kryo 1.7 GHz (DC) | 64 | 2.2 GHz | integrated LTE
810 | H2/2014 | 20 nm | ARM Cortex A57 (QC) + ARM Cortex A53 (QC) | 32/64 | 2.0 GHz | integrated LTE
808 | H1/2015 | 20 nm | ARM Cortex A57 (DC) + ARM Cortex A53 (QC) | 32/64 | 2.0 GHz | integrated LTE
805 | Q1/2014 | 28 nm | Krait 450 (QC) | 32 | 2.7 GHz | integrated LTE
801 | Q4/2013 | 28 nm | Krait 400 (QC) | 32 | 2.5 GHz | integrated LTE
800 | Q2/2013 | 28 nm | Krait 400 (QC) | 32 | 2.3 GHz | integrated LTE
615 | Q3/2014 | 28 nm | ARM Cortex A53 (QC) + ARM Cortex A53 (QC) | 32/64 | 1.7 GHz 1.0 GHz | integrated LTE
602 | Q1/2014 | 28 nm | Krait 300 (QC) | 32 | 1.5 GHz | integrated WiFi
600 | Q1/2013 | 28 nm | Krait 300 (QC) | 32 | 1.9 GHz | integrated WiFi
410 | 1H/2014 | 28 nm | ARM Cortex A53 (QC) + | 32/64 | 1.4 GHz | integrated LTE
400 | Q4/2013 | 28 nm | Krait 300 (QC) or ARM Cortex A7 (QC) | 32 | 1.7 GHz 1.4 GHz | integrated LTE
200 | 2013 | 28 nm | ARM Cortex A5 (QC) or ARM Cortex A7 (QC) | 32 | 1.4 GHz 1.2 GHz | integrated 3G
Main features of the Qualcomm Snapdragoon lines

## Slide 24: 2. Emergence and spread of smartphones (15)
Qualcomm’s Snapdragon 810 platform [65]

## Slide 25: 2. Emergence and spread of smartphones (16)
Qualcomm’s RF-360 Radio Frequency unit [65]

## Slide 26: 2. Emergence and spread of smartphones (17)
Clover Trail+
(2013)
Medfield
(2012)
Merrifield
(2014)
Moorefield
(2014)
Morganfield
(2015?)
Lexington
(2013)
Slayton
(2014)
Riverton
(2015)
Binghampton
(2016)
Z2580-2520
2xSaltwell
32 nm
+XMM 6268/6360/7160
Z2420
1xSaltwell
32 nm
+XMM 6265
Z2480/2460
1xSaltwell
32 nm
+XMM 6260
Z34x0
2xSilvermont
22 nm
+XMM 7160/7260
Z3xxx
2xSilvermont
22 nm
+A-GOLD 620
Zxxxx
2xAirmont
14 nm
+?
Zxxx
2xAirmont
14 nm
+?
Z35xx
4xSilvermont
22 nm
+XMM 7260/2/35
Z5xxx
4xGoldmont
14 nm
+XMM 7360
Intel’s Atom platforms targeting smartphones
(based on [33])
Performance (not to scale)
Morestown
(2010)
Z6xx
1xBonnell
45 nm
+Wireless
module

## Slide 27: 2. Emergence and spread of smartphones (18)
Intel’s XMM line
3G/4G modem + transceiver implemented on two chips
3G/4G modem
Transceiver
Figure: Implementation
example of the two chip
XMM7160 [46]

## Slide 28: 2. Emergence and spread of smartphones (19)
Intel’s effort to optimize their devices from the software point of view
In their 2012 Investor meeting (5/2012) Intel revealed that more than 3000
engineers are working on OS support, among them about 1200 engineers
are dedicated to Android, as indicated below [11].

## Slide 29
3. Emergence and spread of tablets
Notes: 29

## Slide 30: 3. Emergence and spread of tablets (2)
2010: Apple’s iPad with 9.7 “ screen, touch screen and Wi-Fi or additionally wireless
3G broadband internet connection (mobile internet connection), operating under
iOS [12].
Designs giving the final push for rapid spreading of tablets around 2010
From 2009 on: Android-based tablets arrived the market from many vendors.
Figure: Steve Jobs introducing the iPad in 2010 [12]

## Slide 31: 3. Emergence and spread of tablets (3)
Implementation alternatives of tablets-1 [8]

## Slide 32: 3. Emergence and spread of tablets (4)
Intel’s Surface Pro 3
used as a laptop [22]
Intel’s Surface Pro 3
used as a tablet [23]
Implementation alternatives of tablets-2 [8]
2 in 1 tablets (≈ attachable keyboard + touchscreen)
Example: Windows Surface Pro 3 (8/2014)
Aim: Replacing laptops

## Slide 33: 3. Emergence and spread of tablets (5)
Besides smartphones, tablets and all their alternative designs (that provide also keyboard/mouse input, such as convertibles or 2 in 1 designs) have recently the highest growth potential, as indicated in the Figure below (12/1012) [3].
Desktops
Notebooks
Tablets
Figure: Yearly worldwide sales figures of desktops, notebooks and tablets [3]
Rapid increase of tablet sales in the first half of the 2010’s

## Slide 34: 3. Emergence and spread of tablets (6)
Worldwide PC, laptop and tablet shipments 2012 – 2018 [55]
(Shipments in million units)

## Slide 35: 3. Emergence and spread of tablets (7)
1Q/2014 worldwide tablet shipments and market shares by vendors [31]
(Shipments in million units)

## Slide 36: 3. Emergence and spread of tablets (8)
Global market share of tablet OS shipments 2010 - 2014 by quarter [25]

## Slide 37: 3. Emergence and spread of tablets (9)
Clover Trail
(2012)
Oak Trail
(2011)
Bay Trail
(2013)
Cherry Trail
(2015)
Willow Trail
(2015?)
Atom X3
(Sophia 3G)
(2015)
Atom X3
(Sophia LTE)
(2015)
Z2760
2xSaltwell
32 nm
+XMM 6260
W
Z670/650
1xBonnell
45 nm
+ no XMM
W/MeeGo/A
Z37x0
4xSilvermont
22 nm
+XMM 6260/7160
W/A
C3000
2xSilvermont
28 nm
integrated 3G
modem
C3400
4xAirmont
28 nm
integrated LTE
modem
Z4xxx
4xAirmont
14 nm
+XMM 7160/7260
W/A
Z5xxx
4xGoldmont
14 nm
+XMM 7360
W/A
Intel’s platforms targeting tablets
(based on [11])
Performance (not to scale)
Menlow
(2008)
Z5xx
1xBonnell
45 nm
+ no XMM
W/Moblin

## Slide 38: 3. Emergence and spread of tablets (11)
Tablet application processors worldwide market share 2014 (revenue) [57] | 
Apple (USA) | 27 %
Intel (USA) | 19 %
Qualcomm (USA) | 16 %
MediaTek (Taiwan) | 
Samsung (S. Korea) | 
Worldwide market share of application processors used in tablets in 2014
(based on revenue) [57]

## Slide 39
4. Key requirement of mobile devices (tablets, smartphones)
Notes: 39

## Slide 40: 4. Key requirement of mobile devices (tablets, smartphones)
Key requirements of mobile devices (tablets, smartphones)
Connectivity
(3G/4G/Wi-Fi)
Low power operation
4. Key requirement of mobile devices (tablets, smartphones)
(Section 4.1)
(Section 4.2)

## Slide 41
4.1 Low power operation
Notes: 41

## Slide 42: 4.1 Low power operation (3)
Example: Block diagram of Qualcomm’s Snapdragon 820) (2015) [61]

## Slide 43: 4.1 Low power operation (4)
Key criteria for low power microarchitectures
Low processor clock frequency
Narrow microarchitecture
Key criteria for low power microarchitectures
(Section 4.1.2)
(Section 4.1.3)

## Slide 44: 4.1 Low power operation (5)
4.1.2 “Narrow” microarchitectures
Microarchitecture of Intel’s and AMD’s recent traditional processors
they are aiming at high performance/power (in terms of GFLOPS/Watt)
consequently
have wide microarchitectures, as the next example shows:
Example: Width of Intel’s Core 2 (2006) to Skylake (2015) processors underlying
servers to laptops [10]
64-bit
Skylake
We note that AMD introduced 4-wide microarchitectures five years later, along with
the Bulldozer line in 2011.

## Slide 45: 4.1 Low power operation (7)
Key features of ARM’s 32-bit microarchitectures -1 (based on [10])

## Slide 46: 4.1 Low power operation (7a)
Key features of ARM’s 64-bit microarchitectures -2 (based on [10])
Remark: In the Cortex-A9 the NEON FP operates in order.

## Slide 47: 4.1 Low power operation (8)
Block diagram of Apple’s Cyclone core, introduced in the A7 SOC (2013) [48]

## Slide 48: 4.1 Low power operation (9)
Geekbench 3.2 results of recent tablets [49]
3 Cyclone
cores

## Slide 49: 4.1 Low power operation (11)
D = const x fc x Vdd2
4.1.3 Low clock frequency-1
In addition: higher fc requires higher Vdd (Vdd ≈ const x fc).
Basics
Figure: Core voltage (Vdd) vs. clock frequency (fc) for Intel’s Westmere processors [26]

## Slide 50: 4.1 Low power operation (13)
28 nm
20 nm
28 nm
20 nm
Power consumption vs. fc in Samsung's 28 and 20 nm processors [66]

## Slide 51: 4.1 Low power operation (14)
TDP (W) | No. of cores | Graphics | No. of graphics EUs | eDRAM | Base frequency up to (GHz)
4.5 | 2 | HD 515 | 18 | -- | 1.2
15 | 2 | HD 540 | 48 | 64 MB | 2.2
15 | 2 | HD 520 | 24 | -- | 2.6
28 | 2 | HD 550 | 48 | 64 MB | 3.3
35 | 4 | HD 530 | 24 | -- | 2.8
45 | 4 | HD 530 | 24 | -- | 2.9
65 | 4 | HD 530 | 24 | -- | 3.4
91 | 4 | -- | -- | -- | 4.2
Example: Max. base frequency of Skylake models with different TDPs and
configurations (Based on data from [58])
Note that low TDP can be achieved first of all by reducing the core frequency and
limiting the computer resources (cores, GPU EUs) provided.

## Slide 52
4.2 Connectivity
Notes: 52

## Slide 53: 4.2 Connectivity (2)
Simplified view of a platform providing mobile broadband connectivity [59]
PA: Power Amplifier
(DSP)
Modem + Application Processor
(assuming an integrated implementation)
RF

## Slide 54: 4.2 Connectivity (3)
Use of integrated
application processor and modem
Integration of the application processor and the modem
Qualcomm’s MSM product offerings
since ~ 1996
including their Snapdragon families
Use of discrete
application processor and modem
Intel’s Atom line (2008)
except recent Atom X3 (Sophia (2015)
Apple’s own processor designs
(Swift (2012), Cyclone (2013)
E.g.
NVIDIA’s Tegra 2-4, K1 (since 2011)
NVIDIA’s Tegra 4i (2014)
Intel’s Atom X3 (Sophia) (2015)
MediaTek’s 6xxx/8xxx families (since ~ 2009)
except the 81xx line
MediaTek’s 81xx line (2013)
Integration of the application processor and the modem
Samsung’s Exynos 3/4/5/7 families
(since ~ 2010)
Integrating the modem into the chip results in less costs and shorter time to
market.
Qualcomm pioneered this move designing integrated parts already about 1996.

## Slide 55: 4.2 Connectivity (4)
Example of using discrete application processor and modem: The iPhone 6+
PAD: Integrated Power Amplifier-Duplexer
The front side of the
logic board [60]

## Slide 56: 4.2 Connectivity (5)
Example of using an integrated application processor and a modem
(Qualcomm’s Snapdragon 820) [61]

## Slide 57: 4.2 Connectivity (6)
Smartphone application processors worldwide market share in Q1 2014 (revenue) [34] | 
Qualcomm (USA) | 53 %
Apple (USA) | 16 %
MediaTek (Taiwan) | 13 %
Samsung (S. Korea) | 
Spreadtrum (China) | 
Tablet application processors worldwide market share 2014 (revenue) [57] | 
Apple (USA) | 27 %
Intel (USA) | 19 %
Qualcomm (USA) | 16 %
Worldwide market share of smartphone and tablet application processors
in 2014 (based on revenue)

## Slide 58: 4.2 Connectivity (7)
Qualcomm provides single chip solutions
for feature phones, termed as
QSCs (Qualcomm Single Chips).
QSCs integrate the functions of
MSMs
RF Transmitters (RF Tx)
RF Receivers (RF Rx) and
Power manager ICs (PM)
as illustrated on the Figure left [62].
Integrating the application processor, the modem, RF transmitter,
RF receiver and power manager IC onto a single chip
It became feasible for less demanding applications, e.g. for feature phones.
Example: Qualcomm’s QSCs (Qualcomm Single Chips)
Figure: Qualcomm’s integrated QSC [62]

## Slide 59: 4.2 Connectivity (8)
Using PoP (Package on Package) memory
1GB LPDDR3-1600 SDRAM
Figure: Apple’s A7 PoP [63]
Remark
The processor die and the memory die or dies are mounted in the same package.
E.g. In Apple’s A7 Package-on-Package processor, as used in the iPhone 5s.

## Slide 60
5. How leading IT vendors addressed the mobile boom?
5.2 Microsoft’s response to the mobile boom
5.1 Intel’s and AMD’s response to the mobile boom
Notes: 60

## Slide 61
5.1 Intel’s and AMD’s response to the mobile boom
Notes: 61

## Slide 62: 5.1 Intel’s and AMD’s response to the mobile boom (2) (1)
Total shipments of smartphones vs. PCs and tablets 2011-2017 [28]
Source: Gartner (2013)
Smartphone and tablet shipments
will vastly exceed PC shipments
(desktops and notebooks)
in a few years

## Slide 63: 5.1 Intel’s and AMD’s response to the mobile boom (4)
Evolution of Intel’s basic architectures [Based on 2]
2008
2-wide
in-order
4-wide
out-of-order
2-wide
in order
2-wide
out-of-order
2-wide
out-of-order
2015
Broadwell
14 nm

## Slide 64: 5.1 Intel’s and AMD’s response to the mobile boom (5)
2011
2012
2013
~10/2011
~5/2012
1/2014
1/2011
5/2013
AMD
Bulldozer
Family 15h
AMD
Family 14h/16h
Optimized Power/Performance
Microarchitecture
Low Power
Microarchitecture
Bulldozer
Models 00h-0Fh
32nm
Piledriver
Models 10h-1Fh
32 nm
Steamroller
Models 30h-3Fh
28nm
Jaguar
28nm
Bobcat
40nm
Evolution of AMD’s basic architectures
Puma
28nm
2014
4/2014
2-wide
out-of-order
2-wide
out-of-order
2-wide
out-of-order
4-wide
out-of-order

## Slide 65: 5.1 Intel’s and AMD’s response to the mobile boom (7)
Global unit sales of current generation video game consoles 2008-2014 [64]
(in million units)

## Slide 66: 5.1 Intel’s and AMD’s response to the mobile boom (9)
AMD’s technologies developed to reduce power consumption (2008-2014) [27]

## Slide 67
5.2 Microsoft’s response to the mobile boom
Notes: 67

## Slide 68: 5.2 Microsoft’s response to the mobile boom (1)
5.2 Microsoft’s response to the mobile boom-1
Worldwide software revenues in 2013 [25]

## Slide 69: 5.2 Microsoft’s response to the mobile boom (4)
Surface Pro lines
Microsoft’s Surface family of tablets
Surface lines
First Surface tablets are NVIDIA’s Tegra based
and run under Windows RT/Windows 8.1
Recent Surface tablets are Intel’s Atom based
and are running under Windows 8.1
Surface Pro tablets are Core 2 based
and run under Windows 8
or subsequent Windows versions
High end models
Less expensive models
Overview of the Microsoft’s Surface family of tablets

## Slide 70: 5.2 Microsoft’s response to the mobile boom (5)
Model | Intro | Processor | Word length | Core nr. | OS
Surface | 10/2012 | Tegra 3 | 32-bit | 4 | Windows RT
Surface 2 | 10/2013 | Tegra 4 | 32-bit | 5 | Windows RT/Windows 8.1
Surface 3 | 05/2015 | Atom X7-Z8700 Airmont core | 64-bit | 4 | Windows 8.1
Table: Microsoft’s ARM/Intel Atom-based Surface RT /Surface 2 tablets
Microsoft’s Surface tablets-2
Main features of Microsoft’s Surface tablet lines

## Slide 71: 5.2 Microsoft’s response to the mobile boom (6)
Model | Intro | Processor | Word length | Core nr. | OS
Surface Pro | 02/2013 | Ivy Bridge i5 | 64-bit | 2 | Windows 8 Pro
Surface Pro 2 | 10/2013 | Haswell i5 | 64-bit | 2 | Windows 8.1 Pro
Surface Pro 3 | 06/2014 | Haswell i3/i5/i7 | 64-bit | 2 | Windows 8.1 Pro
Surface Pro 4 | 11/2015 | Skylake m3/i5/i7 | 64-bit | 2 | Windows 10 Pro
Table: Microsoft’s Intel Core 2-based Surface Pro tablets
Microsoft’s Surface tablets-3
Main features of Microsoft’s Surface Pro tablet lines

## Slide 72: 5.2 Microsoft’s response to the mobile boom (7)
Windows Surface Pro 3 (8/2014)
2 in 1 tablet 12”
Aim: Replacing laptops
Intel’s Surface Pro 3
used as a laptop [22]
Intel’s Surface Pro 3
used as a tablet [23]

## Slide 73: 5.2 Microsoft’s response to the mobile boom (8)
Early financial performance of Microsoft’s Surface business [24]