## Slide 1
Dezső Sima
Intel’s Core family - TOCK lines
Core 2 to Skylake
September 2015
Vers. 1.0

## Slide 2
Contents
1. Introduction
2. The Core 2 line
3. The Nehalem line
4. The Sandy Bridge line
5. The Haswell line
6. The Skylake line
7. The Kaby Lake line

## Slide 3
1. Introduction
Notes: 3

## Slide 4: 1. Introduction (1)
The evolution of Intel’s basic Core family
Figure 1.1: Intel’s Tick-Tock development model (Based on [1])
1. Introduction
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
1. gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
Skylake
New
Microarchi.
14 nm
TOCK
6. gen.

## Slide 5
Basic architectures | Basic architectures and their shrinks
Pentium 4 (Prescott) | 2005 90 nm Pentium 4 2006 65 nm Pentium 4
Core 2 | 2006 65 nm Core 2 2007 45 nm Penryn
Nehalem | 2008 45 nm Nehalem 2010 32 nm Westmere
Sandy Bridge | 2011 32 nm Sandy Bridge 2012 22 nm Ivy Bridge
Haswell | 2013 22 nm Haswell 2014 14 nm Broadwell
Skylake | 2015 14 nm Skylake ? 14 nm Kaby Lake ? 10 nm Cannonlake
1. Introduction (2)
Basic microarchitectures and their related shrinks
Considered from the Pentium 4 Prescott (the third core of Pentium 4) on.

## Slide 6
Changing the design paradigm to cope with raising dissipation
In 2003 Intel shifted the focus of their processor development from the pure performance goal
to the aspect of performance per watt, as stated in a slide from 4/2006, see below.
Figure 1.3: Intel’s plan to develop their manufacturing technology and processor lines
revealed at a shareholder’s meeting back in 4/2006 [74]
1. Introduction (3)

## Slide 7
High performance/power
(e.g. GFLOPS/Watt)
Traditional processors
Tablets and smartphones
Low power
(Watt)
(Number of operating hours)
With the advent of mobile devices (about 2006) a new design paradigm arose for those devices.
Mobile devices require long operating hours i.e. low power consumption, this is contrast to the
design paradigm of traditional processors, as indicated below.
1. Introduction (4)
Changing the design paradigm for mobile processors

## Slide 8: 1. Introduction (5)
Key requirements for low power microarchitectures
Low processor clock frequency
Narrow microarchitecture
Key requirements for low power microarchitectures

## Slide 9: 1. Introduction (6)
2005
2007
2010
2009
(A9 replacement
for low-end
devices)
32-bit
Example: Width of ARM’s 32-bit CPUs used in most tablets and smartphones [10]
a) Low power CPUs need narrow microarchitectures

## Slide 10: 1. Introduction (7)
By contrast:
Intel’s and AMD’s recent processor lines
aims at high performance/power (in terms of GFLOPS/Watt)
accordingly
have 4-wide microarchitectures, as the next example shows:
64-bit
Example: Width of Intel’s Core 2 to Haswell processors underlying servers to laptops [10]

## Slide 11: 1. Introduction (8)
Consequences for Intel and AMD-1
Intel’s and AMD’s traditional microarchitectures are not suited for mobile devices.
If they want to become competitive with ARM designed ones, they need to design
new, narrow (e.g. 2-wide) low-power microarchitectures.

## Slide 12: 1. Introduction (9)
Emergence of Intel’s Atom line aiming for tablets and smartphones [] [2]
2008
2-wide
in-order
4-wide
out-of-order
2-wide
in order
2-wide
out-of-order
2-wide
out-of-order
Broadwell
14 nm
2015

## Slide 13
b) Low power CPUs need low base clock frequencies
High base clock frequency
(typically 2-4 GHz)
Traditional CPUs
Mobile CPUs
Relative low base clock frequency
(typically 1-2 GHz)
( D = const x fc x V2, in addition higher fc requires higher V)
1. Introduction (10)

## Slide 14
TDP (W) | No. of cores | Graphics | No. of graphics EUs | eDRAM | Base frequency (GHz)
4.5 | 2 | HD 515 | 18 | -- | 1.2
15 | 2 | HD 540 | 48 | 64 MB | 2.2
15 | 2 | HD 520 | 24 | -- | 2.6
28 | 2 | HD 550 | 48 | 64 MB | 3.3
35 | 4 | HD 530 | 24 | -- | 2.8
45 | 4 | HD 530 | 24 | -- | 2.9
65 | 4 | HD 530 | 24 | -- | 3.4
91 | 4 | -- | -- | -- | 4.2
Example: The max. base frequency of Skylake models resulting in different TDPs and
configurations (Based on data from [202])
Note that low TDP can be achieved first of all by reducing the core frequency and limiting
the computer resources (cores, GPU EUs) provided.
1. Introduction (11)

## Slide 15: 1. Introduction (12)
Figure : Overview of Intel’s Tick-Tock model (Based on [3])
New microarch.,
64-bit
New microarch.: 4-wide core,
128-bit SIMD/FP, shared L2 , no HT
11/2007
01/2006
90nm
130nm
TICK TOCK
2 YEARS
2 YEARS
2 YEARS
65nm
TICK Pentium 4 / Cedar Mill
TOCK Core 2
2 YEARS
New microarch.
New microarch.,
hyperthreading (HT)
Pentium 4 /Northwood
TICK TOCK
TICK TOCK
Pentium 4 /Prescott
Pentium 4 /Willamette
07/2006
11/2008
New microarch.: 256-bit AVX,
ring bus, integr. GPU
11/2000
01/2002
02/2004
Key new features of the ISP
and the microarchitecture
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
180nm
AVX2,
L4 cache (discrete eDRAM), FIVR
06/2013
09/2014
Shared Virtual Memory
08/2015
ISP,
Memory Side $ (eDRAM), No FIVR
In package integr. GPU
14nm
2 YEARS
TICK Broadwell
TOCK Skylake
New microarch.: integrated MC, QPI,
(inclusive) L3, HT
Intel’s Tick-Tock model for the P4 and Core lines

## Slide 16
Per Generation
Cumulative
Pentium M Dothan
Core 2
Penryn
NHM (w/o SMT)
WSM
SNB
IVB
HSW
BRW
1.8
1.7
1.6
1.5
1.4
1.3
1.1
1.2
1
2
1.9
20%
18%
16%
14%
12%
10%
8%
6%
4%
2%
0%
24%
22%
SKL
Single thread IPC in Intel’s basic architectures (Based on [195])
Note that Intel raised IPC in the Core family only less then 2-times in about 10 years.

## Slide 17: 1. Introduction (14)
Servers
Recent main product categories of Intel
Smartphones
Tablets
Atom lines
Xeon lines
(X86/Itanium)
Desktops/Laptops
(Client computing)
Core lines
(Basic architectures)
Atom lines
(+ LP Core models)
Recent main product categories of Intel and underlying processor lines

## Slide 18: 1. Introduction (15)
Server platforms classified according to the number of processors supported
DP (2S)
server platforms
Server platforms
Platforms for more than four servers
2- processor server platforms
(2-socket server platforms)
MP (4S)
server platforms
4-processor server platforms
(4-socket server platforms)
(Server platforms for
more than four sockets)
Uniprocessor server platforms
(UP-server platforms)
1-processor server platforms
(1-socket server platforms)
Multiprocessor server platforms
Server platforms supporting more than one processor
(Multi-socket server platforms)

## Slide 19
Designation of the platform | Platform topology | Processor | Technology | Max. no. of cores (nC) | Year of introduction | Processor socket | MCH/PCH | Highest mem./ speed grade | No. of mem. channels (nM)
Anchor Creek | Off-die MC | Pentium D | 90 nm | 2x1 | 5/2005 | LGA 775 | 945-955 | DD2-667 | 2
Bridge Creek |  | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
Salt Creek |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series (Bearlake) | DDR3-1067 | 2
Boulder Creek |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series (Eaglelake) | DDR3-1067 | 2
Kings Creek | On-die MC | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series (Ibex Peak) | DDR3-1333 | 2
 |  | Clarkdale | 32 nm | 2C+G | 1/2010 | LGA 1156 | 5 Series (Ibex Peak) |  | 
 |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | LGA 1155 | 6 series (Cougar Point) | DDR3-1333 | 2
Sugar Bay |  |  |  |  |  |  |  |  | 
 |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 | LGA 1155 | 7 series (Panther Point) | DDR3-1600 | 2
 |  | Haswell | 22 nm | 4C+G | 6/2013 | LGA 1155 | 8 Series (Lynx Point) | DDR3-1600 | 2
 |  | Haswell refresh | 22 nm |  | 5/2014 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1666 | 
 |  | Broadwell | 14 nm |  | 6/2015 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1866 | 
 |  | Skylake | 14 nm | 4C+G | 8/2015 | LGA 1151 | Series (Sunrise Point) | DDR4-2133 | 2
Intel’s Core-based mainstream DT platforms
1. Introduction (16)

## Slide 20: 1. Introduction (17)
Key features of the evolution of Intel’s Core-based mainstream DT platforms
Their core count rose soon (already in 2007) to 4 and remain at this figure.
Two memory channels are used to connect memory.
Up to the Penryn memory is connected via the MCH thereafter immediately via the processor.
In a 10 year period memory speed rose about three times.

## Slide 21
Intel’s Core based Extreme Edition (E-Series) DT platforms
1. Introduction (18)
Processor | Techn. | Date of intro. | Max. no. of cores | Platform topology | Highest mem./ speed | PCIe lanes | No. of mem. channels | MCH | Processor socket
1. G. Nehalem EE | 45 nm | 11/2008 | 4C | On-die MC | DDR3-1067 | 36 PCIe 2.0 on the X58 | 3 | X58 (Tylersburg) | LGA 1366
Westmere-EE | 32 nm | 3/2010 | 6C |  |  |  |  |  | LGA 1366
Sandy Bridge-E | 32 nm | 11/2011 | 6C |  | DDR3-1600 | 40 PCIe 2.0 on the die | 4 | X79 (Patsburg) | LGA 2011
Ivy Bridge-E | 22 nm | 9/2013 | 6C |  | DDR3-1866 | 40 PCIe 3.0 on the die | 4 |  | LGA 2011
Haswell-E | 14 nm | 8/2014 | 8C |  | DDR4-2133 |  | 4 | X99 (Wellsburg) | LGA 2011-3

## Slide 22: 1. Introduction (19)
The Extreme Edition lines (E-lines) aim at high performance desktops for hardcore gamers
and graphics enthusiasts.
Key features of Intel’s Extreme Edition lines (E-lines):
They provide typically
more cores
more PCIe lanes (either on the PCH or on the die)
more memory channels (to appropriately service more processing resources)
than the standard desktop platform,
they do not provide integrated graphics, as it is assumed that the installation is intended
to provide high quality graphics by attaching multiple discrete graphics cards.
they are unlocked, nevertheless
They have a high power consumption of 130 to 150 W.
Key features of Intel’s Core-based Extreme Edition lines (E-lines)

## Slide 23
Platform | Platform topology | Date of intro. | Processor | Technology | Core count (up to) | No. and speed of memory channels/socket | Kind of connecting memory Socket
Truland MP | SMP w/dual FSBs | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 90 nm | 1C | 1x DDR2-400/socket | 4 serial channels (IMI) via MCH LGA 604
 |  | 11/2005 | Xeon 7000 (Paxville MP) | 90 nm | 2x1C |  | 
 |  | 8/2006 | Xeon 7100 (Tulsa) | 65 nm | 2C |  | 
Caneland | SMP w/Quad FSBs | 9/2007 | Xeon 7200 Tigerton DC (Core 2) | 65 nm | 2C | 1x DDR2-667/socket (FB-DIMM) | 4 serial FB-DIMM channels via MCH LGA 604
 |  | 9/2007 | Xeon 7300 Tigerton QC (Core 2) | 65 nm | 2x2C |  | 
 |  | 9/2008 | Xeon 7400 (Dunnington) (Penryn) | 45 nm | 6C |  | 
Boxboro-EX | NUMA fully connect. | 3/2010 | Nehalem-EX (Xeon 7500/ (Beckton) | 45 nm | 8C | 8x DDR3-1067/socket | 4 serial channels (SMI) /processor LGA 1567
 |  | 4/2011 | Westmere-EX (E7-4800) | 32 nm | 10C |  | 
Brickland | NUMA fully connect. | 2/2014 | Ivy Bridge-EX (E7-4800 v2) | 22 nm | 15C | 8x DDR3-1600/socket | 4 parallel channels (SMI2)/processor LGA-2011-1
 |  | 5/2015 | Haswell-EX (E7-4800 v3) | 22 nm | (14C) 18C | 8x DDR4-1866/socket | 
Intel’s Core-based MP platforms
1. Introduction (20)

## Slide 24: 1. Introduction (21)
Key features of the evolution of Intel’s Core-based MP platforms
Their core count raises more or less according to Moore’s rule (with a noticeable slow down
recently).
The number of memory channels rose rapidly from 1 per socket to 8 per socket to provide
enough memory bandwidth for the increasing number of cores.
Here we note that n cores need n-times higher memory bandwidth.
Memory speed rose about 4 times in a period of 10 years.
With the Nehalem basic architecture platform topology has changed from SMP to NUMA.

## Slide 25: 1. Introduction (22)
Remark: Classification of multiprocessor platforms according to their memory architecture
SMPs
(Symmetrical MultiProcessor)
Multiprocessor platforms
classified according to their memory architecture
NUMAs
Multiprocessors (Multi socket system)
with Non-Uniform Memory Access
Multiprocessors (Multi socket system)
with Uniform Memory Access (UMA)
Typical examples
Processor
MCH
ICH
FSB
Processor
E.g. DDR2-533
ESI
E.g. DDR3-1333
Processor
IOH1
QPI
QPI
ICH
ESI
QPI
E.g. DDR3-1333
Processor
All processors access main memory by the same
mechanism, (e.g. by individual FSBs and an MCH).
A particular part of the main memory can be accessed
by each processor immediately, other parts remotely.
1ICH: I/O hub
ESI: Enterprise System Interface

## Slide 26
*
*
*
*
Transfer rate (MT/s)
50
100
500
Year
03
05
01
02
04
06
07
08
1000
3000
200
2000
~ 2*/4 years
DDR2
533
DDR2
667
DDR2 800
DDR3
1600
09
11
2010
12
13
15
DDR3
1067
2000

14
*
*
DDR3
1333
*
DDR4/2133
DDR3/1866
*
*
*
DDR
333
~ 2*/8 years
DDR
266
Historical increase of memory transfer rates in Intel’s DT and MP platforms
x
x
x
x
x
*
DDR
400
DDR2
667
DDR3
1600
DDR3
1866
DDR
400
DDR3
1067
DT
MP
1. Introduction (23)

## Slide 27
Intel Core generation | Graphics generation | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Westmere | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 7th | HD 2500 | GT1 | 1 (6 EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Evolution of main features of Intel’s graphics families (based on [174])
1. Introduction (24)

## Slide 28: 1. Introduction (25)
Key features of the evolution of Intel’s integrated graphics families
Intel’s graphics implementations are subdivided into
graphics generations (5th to 9th) and
graphics technology levels (GT1-GT4).
Graphics generations are bound to the basic architectures.
The graphics technology levels indicate the number of graphics slices (replicable sets of
graphics EUs)
The number of graphics EUs is increasing more or less according to Moore’s rule
(from 12 in 2010 to 72 in 2015)
With the Haswell basic architecture graphics became eDRAM support (first 64 MB
then 128 MB)
There is continuous support of newer versions of graphics APIs and of OpenCL.

## Slide 29: 1. Introduction (26)
Graphics performance increase of subsequent Core generations [196]
Skylake
Broadwell
Haswell
Ivy Bridge
Sandy Bridge

## Slide 30
2. The Core 2 line
2.1 Introduction
2.2 Major innovations of the Core 2 line
2.4 Die plot of the Core 2
2.5 Overview of Core 2 based processor lines
2.3 Performance leadership change between
Intel and AMD achieved by the Core 2
Notes: 30

## Slide 31
2.1 Introduction
Notes: 31

## Slide 32: 2.1 Introduction (1)
2.1 Introduction-1
The next line became based primarily on the Pentium M – Intel’s first mobile line
since for its designs dissipation reduction was a key issue.
(The Pentium M line was a 32-bit line with 3 subsequent cores, designed at
Intel’s Haifa Research and Development Center) thus the Core 2 was developed also there.
The Pentium 4 line was cancelled due to unmanageable high dissipation figures
of its third core (the 90 nm Prescott core)
(caused primarily by the design philosophy of the line
that preferred clock frequency over core efficiency for increasing performance).
The Haifa team had no experience with multithreading.
The Core microarchitecture does not support multithreading.
For the development of the next processor line dissipation became the key design issue.

## Slide 33: 2.1 Introduction (2)
Figure : Intel’s Tick-Tock development model (Based on [1])
Figure 4.1.1: Intel’s Tick-Tock development model (Based on [1])
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
1. gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
Skylake
New
Microarchi.
14 nm
TOCK
6. gen.
The Core 2 is Intel’s 1. generation new microarchitecture, it is using 65 nm line width.
First delivered in 6/2006.
2.1 Introduction-2

## Slide 34: 2.1 Introduction (3)
Figure : Overview of Intel’s Tick-Tock model (Based on [3])
New microarch.,
64-bit
New microarch.: 4-wide core,
128-bit SIMD/FP, shared L2 , no HT
11/2007
01/2006
90nm
130nm
TICK TOCK
2 YEARS
2 YEARS
2 YEARS
65nm
TICK Pentium 4 / Cedar Mill
TOCK Core 2
2 YEARS
New microarch.
New microarch.,
hyperthreading (HT)
Pentium 4 /Northwood
TICK TOCK
TICK TOCK
Pentium 4 /Prescott
Pentium 4 /Willamette
07/2006
11/2008
New microarch.: 256-bit AVX,
ring bus, integr. GPU
11/2000
01/2002
02/2004
Key new features of the ISP
and the microarchitecture
The Core 2 line
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
180nm
AVX2,
L4 cache (discrete eDRAM), FIVR
06/2013
09/2014
Shared Virtual Memory
08/2015
ISP,
Memory Side $ (eDRAM), No FIVR
In package integr. GPU
14nm
2 YEARS
TICK Broadwell
TOCK Skylake
New microarch.: integrated MC, QPI,
(inclusive) L3, HT

## Slide 35
2.2 Major innovations of the Core 2 line
2.2.1 4-wide core
2.2.3 Smart L2 cache
2.2.4 Innovations in power management
2.2.2 128-bit SIMD and FP units
Notes: 35

## Slide 36: 2.2.1 4-wide core (1)
2.2 Major innovations of the Core 2 line
2.2.1 4-wide core
This is the key benefit of the Core 2 family.
By contrast
both Intel’s previous Pentium 4 family and AMD’s K8 have only 3-wide cores,
as the next Figures show.
It means 4-wide front end and retire unit.

## Slide 37: 2.2.1 4-wide core (2)
Figure 2.2.1.1: Block diagram of Intel’s Core 2 microarchitecture [4]

## Slide 38: 2.2.1 4-wide core (3)
Figure 2.2.1.2: Block diagram of Intel’s Pentium 4 microarchitecture [5]
Retire width: 3 instr./cycle

## Slide 39: 2.2.1 4-wide core (4)
Figure 2.2.1.3: Block diagram of AMD’s K8 microarchitecture[4]

## Slide 40: 2.2.2 128-bit wide SIMD and FP units (1)
a) Overview of the x86 ISA extensions in Intel’s processor lines
2.2.2 128-bit wide SIMD and FP units
They aim at providing enhanced media support.

## Slide 41: 2.2.2 128-bit wide SIMD and FP units (2)
Advanced Encryption Standard
Advanced Vector Extension
Fused Multiply-Add instr.
Streaming SIMD Extensions
MultiMedia eXtensions
Northwood (Pentium 4)
Ivy Bridge
Pentium III
Pentium 4
Core 2
Overview of Intel’s x86 ISA extensions (based on [18])

## Slide 42: 2.2.2 128-bit wide SIMD and FP units (3)
Norhwood
Northwood (Pentium4)
Northwood (Pentium4)
8 MM registers (64-bit),
aliased on the FP Stack registers
8 XMM registers (128-bit)
16 XMM registers (128-bit)
16 YMM registers (256-bit)
Ivy Bridge
Pentium MMX
Pentium 4
Core 2
Pentium III
Register spaces provided by Intel’s x86 ISA extensions (based on [18])

## Slide 43: 2.2.2 128-bit wide SIMD and FP units (4)
Illustration of the available SIMD register spaces of the MMX to SSE3/SSSE3 ISA
extensions in 32- and 64-bit ISAs [162]

## Slide 44: 2.2.2 128-bit wide SIMD and FP units (5)
Norhwood
Northwood (Pentium4)
128-bit FX, FP SIMD with
32/16/8-bit FX, 32-bit FP ops.
Support of MM/3D
DSP-oriented FP enhancements,
enhanced thread manipulation
Diverse arithmetic enhancements
64-bit FX SIMD with
32/16/8-bit operands (ops)
Support of MM
128-bit FX, FP SIMD with
64/32/16/8-bit FX, 64/32-bit FP,
Support for MPEG-2, video, MP3
Media acceleration
(video encoding, MM, gaming)
Accelerated string/text manip.,
appl. targeted acceleration
Accelerated encription operations
256-bit FX, FP SIMD with
64/32/16/8-bit FX, 64/32-bit FP
Ivy Bridge
Pentium III
Pentium 4
Core 2
Intel’s x86 ISA extensions - the operations introduced (based on [18])

## Slide 45: 2.2.2 128-bit wide SIMD and FP units (6)
SSSE3 provide 32 instructions (represented by 14 mnemonics) to accelerate computations on
packed integers.
These include:
Overview of the Supplemental Streaming SIMD Extension (SSSE3) of the Core 2 ISA
[161]
• Twelve instructions that perform horizontal addition or subtraction operations (operations
on adjacent numbers.
• Six instructions that evaluate absolute values.
• Two instructions that perform multiply and add operations and speed up the evaluation
of dot products.
• Two instructions that accelerate packed-integer multiply operations and produce integer
values with scaling.
• Two instructions that perform a byte-wise, in-place shuffle according to the second
shuffle control operand.
• Six instructions that negate packed integers in the destination operand if the signs of the
corresponding element in the source operand is less than zero.
• Two instructions that align data from the composite of two operands.

## Slide 46: 2.2.2 128-bit wide SIMD and FP units (7)
Northwood (Pentium 4)
1 full + 1 simple (moves/stores)
64-bit FP/SSE EUs
2 x 128-bit FP EUs +
3 x 128-bit SSE EUs
256-bit SSE EUs
2 x 32-bit FX MMX EUs
2 x 32-bit MMX,
2 x 32-bit SSE EUs
Ivy Bridge
Pentium III
Pentium 4
Core 2
SIMD execution resources in Intel’s basic processors (based on [18])

## Slide 47: 2.2.2 128-bit wide SIMD and FP units (8)
The Core 2 has 128-bit wide and more FP and SSE execution units than Pentium 4 or AMD’s K8,
as detailed below.
b) Contrasting the number of 128-bit wide execution units in Intel’s Pentium 4, Core 2
and AMD’s K8 -1
The next Figure demonstrates it.
Core 2
two 128-bit FP units
three 128-bit SSE units
Pentium 4
single 64-bit FP/SSE unit
single 64-bit FP/SSE move unit
AMD K8
two 64-bit FP/SSE units
single 64-bit FP/SSE move unit

## Slide 48: 2.2.2 128-bit wide SIMD and FP units (9)
FP/SSE
K8 Execution Units
b) Contrasting the number of 128-bit wide execution units in Intel’s Pentium 4, Core 2
and AMD’s K8 -2 [159], [160]

## Slide 49: 2.2.2 128-bit wide SIMD and FP units (10)
Core 2’s achieved performance boost for gaming apps vs. AMD’s Athlon 64 FX60 [13]

## Slide 50: 2.2.3 Shared L2 cache (1)
Pentium 4-based DCs
Core 2-based DCs
2.2.3 Shared L2 cache
Core1
Core2
L2 Cache
L2 Cache
Core1
Core2
L2 Cache
Figure 2.2.3.1: Core’s shared L2 cache vs. Pentium 4’s private L2 caches
Private
Shared
In the Core 2 Intel makes use a shared L2 cache instead of private L2 caches and designates it
as smart L2 cache, as shown below.

## Slide 51: 2.2.3 Shared L2 cache (2)
Benefits of shared caches vs. private caches
Dynamic cache allocation to the individual cores
Data sharing (no replicated data)
+ 2x bandwidth to L1 caches.

## Slide 52: 2.2.3 Shared L2 cache (3)
Drawbacks of shared caches
Shared caches combine memory access patterns
Reduce the efficiency of hardware prefetching vs private caches.
Choice between shared and private caches
Design decision depending on
whether benefits or drawbacks dominate as far as performance is concerned.
Trend
Core 2 prefers a shared L2 cache
Nehalem prefers private L2 caches
POWER5 prefers shared L2 cache
POWER6 prefers private L2 caches
This trend is due to the fact that efficient data prefetching became more important than
dynamic cache allocation or data sharing.

## Slide 53: 2.2.3 Shared L2 cache (4)
Intel’s first hardware prefetcher appeared subsequently in the Pentium 4 family,
associated with the L2 cache (one instruction and one data prefetcher (11/2000).
Principle of operation of the L2 hardware prefetcher
it monitors data access patterns and prefetches data automatically into the L2 cache,
it attempts to stay 256 bytes ahead of the current data access location,
the prefetcher remembers the history of cache misses to detect concurrent,
independent data streams that it tries to prefetch ahead of its use.
Remarks
Intensive use of hardware prefetchers -1 [9]
Intel’s first on-die L2 cache debuted only about two years earlier (8/1998),
in the second core of the Pentium II based Celeron line (called the Mendocino core,
built on 250 nm technology, with an L2 size of 128 KB)1,2.
1 The first Celeron model debuted in 4/1998, it was the low cost alternative to Pentium II,
and was designated as Cavington.
It was manufactured on 250 nm, run at 266 MHz, did not include an L2 cache and had 7.5 mtrs.
The second core of the Celeron line was launched in 8/1998 already with an L2 cache, run
at 266 and 300 MHz and incorporated 19,2 mtrs.
2Note: The debut of L2 was corrected in 29/10/2014.

## Slide 54: 2.2.3 Shared L2 cache (5)
8 prefetchers in the two-core processor
2 data and 1 L1 instruction prefetchers per core,
able to handle multiple simultaneous patterns.
2 prefetchers in the L2 cache
tracking multiple access patterns per core.
Intensive use of hardware prefetchers -2 [11]

## Slide 55: 2.2.3 Shared L2 cache (6)
Figure 2.2.3.2: Hardware prefetchers within the Core 2 microarchitecture [11]
Hardware prefetchers in the Core 2 microarchitecture

## Slide 56: 2.2.4 Innovations in power management (1)
2.2.4 Innovations in power management
Shutting off not needed functional units of the processor
Platform Thermal Control

## Slide 57: 2.2.4 Innovations in power management (2)
Green units not needed
for the given operation,
they can be shut off.
Shutting off not needed functional units of the processor [11]

## Slide 58: 2.2.4 Innovations in power management (3)
Platform Thermal Control [11], [20]
Digital
Thermal Sensors
(DTS) on the dies,
instead of
analog diodes,
providing
digital data,
scanned by
dedicated logic.
(Platform Environment Control Interface)
A single wire proprietary interface with
transfer rates of 2 kbit/s-2 Mbit/s)
DTSs report the difference between the
current temperature and the throttle point,
at which the processor reduces speed.
PECI

## Slide 59: 2.2.4 Innovations in power management (4)
Possible solution for the Platform Thermal Control Manager [88]
Figure 2.2.4.1: The aSC7621 hardware monitor with fan control and PECI from Andigilog
(Remote Sensor)
(Remote Sensor
CPU/Graphics)
(ASIC (Application Specific IC/Microcontroller)

## Slide 60
2.3 Performance leadership change between Intel and AMD achieved by the Core 2
Notes: 60

## Slide 61: 2.3 Performance leadership change between Intel and AMD (1)
AMD’s K8-based processors became the performance leader, first of all on the DP and MP
server market, where the 64-bit direct connect architecture has clear benefits
vs Intel’s 32-bit Pentium 4 based processors using shared FSBs to connect processors
to north bridges.
integrated memory controllers and
high speed point-to-point serial buses (the HyperTransport bus)
used to connect processors to processors and processors to south bridges.
Performance leadership change between Intel and AMD achieved by the Core 2
In 2003 AMD introduced their K8-based processors implementing
the 64-bit x86 ISA and
the direct connect architecture concept, that includes

## Slide 62: 2.3 Performance leadership change between Intel and AMD (2)
Figure 2.3.1: DP web server performance comparison: AMD Opteron 248 vs. Intel Xeon 2.8 [6]
Example 1: DP web-server performance comparison (2003)

## Slide 63: 2.3 Performance leadership change between Intel and AMD (3)
“In the extensive benchmark tests under Linux Enterprise Server 8 (32 bit as well as 64 bit), the AMD Opteron made a good impression.
Especially in the server disciplines, the benchmarks (MySQL, Whetstone, ARC 2D, NPB, etc.) show quite clearly that the Dual Opteron puts the Dual Xeon in its place”.
Example 2: Summary assessment of extensive benchmark tests contrasting
dual Opterons vs dual Xeons (2003) [7]

## Slide 64: 2.3 Performance leadership change between Intel and AMD (4)
two 128-bit FP units and three 128-bit SSE units compared to
This situation has completely changed in 2006 when Intel introduced their Core 2
microarchitecture,
Intel regained performance leadership vs AMD.
This and further enhancements of the Core microarchitecture, detailed subsequently,
resulted in record breaking performance figures.
a 4-wide front-end and retire unit compared to the 3-wide K8,
The Core 2 has
two 64-bit FP/SSE units and a single 64-bit FP/SSE move unit available in the K8.

## Slide 65: 2.3 Performance leadership change between Intel and AMD (5)
Webserver Performance |  |  |  |  | 
 | MSI K2-102A2M Opteron 275 | MSI K2-102A2M Opteron 280 | Opteron 280 vs. Opteron 275 | Extrapolated Opteron 3 GHz | Xeon 5160 3 GHz
Jsp - Peak | 144 | 154 | 7% | 182 | 230
AMP - Peak | 984 | 1042 | 6% | 1178 | 1828
Jsp: Java Server Page performance
AMP: Apache/MySQL/PHP
Example: DP web-server performance comparison (2006)
Figure 2.2.1.8: DP web server performance comparison:
AMD Opteron 275/280 vs. Intel Xeon 5160 [8]
Remark
Both web-server benchmark results were published from the same source (AnandTech)

## Slide 66
2.4 Die plot of the Core 2
Notes: 66

## Slide 67: 2.4 Die plot of the Core 2 (1)
143 mm2
291 mtrs
2.4 Die plot of the Core 2 [163]

## Slide 68
2.5 Overview of Core 2 based processor lines
Notes: 68

## Slide 69: 2.5 Overview of Core 2 based processor lines (1)
2.5 Overview of Core 2 based processor lines
Servers
DP-Servers
MP-Servers
51xx, 2C Woodcrest, 6/2006
53xx, 2x2, Clowertown, (2xWoodcrest) 11/2006
72xx, 2C, Tigerton DC, (2xMP-enhanced SC Woodcrest) 9/2007
73xx, 2x2C, Tigerton QC, (2xMP-enhanced DC Woodcrest) 9/2007
UP-Servers
30xx, 2C, Conroe, 9/2006
30xx, 2C, Allendale 1/2007
32xx, 2x2C, Kentsfield (2xConroe) 1/2007
Mobiles
T5xxx/T7xxx, 2C ,Merom 8/2006
Based on [43]
Desktops
E6xxx/E4xxx, 2C, Core 2 Duo, (Conroe) 7/2006
X6800 Core 2 Extreme, 2C, (Conroe) 7/2006
E6xxx/E4xxx, Core 2 Duo, 2C, (Allendale) 1/2007
Q6xxx Core 2 Quad, 2x2C (Kentsfield) (2xConroe) 1/2007
QX6xxx Core 2 Extreme Quad, 2x2C, (Kentsfield XE) 11/2006

## Slide 70
3. The Nehalem line
3.1 Introduction to the 1. generation Nehalem line
(Bloomfield)
3.2 Major innovations of the 1. gen. Nehalem line
3.3 Major innovations of the 2. gen. Nehalem line
(Lynnfield)
Notes: 70

## Slide 71
3.1 Introduction to the 1. generation Nehalem line (Bloomfield)
Notes: 71

## Slide 72: 3.1 Introduction to the 1. generation Nehalem line (Bloomfield) (1)
3.1 Introduction to the 1. generation Nehalem line (Bloomfield)
Developed at Hillsboro, Oregon, at the site where the Pentium 4 emerged.
Experiences with HT
Nehalem became a multithreaded design.
The design effort took about five years and required thousands of engineers
(Ronak Singhal, lead architect of Nehalem) [37].
(Core i7-9xx (Bloomfield)) 4C in 11/2008
First implementation of the Nehalem microarchitecture appeared in the desktop segment
Figure : Intel’s Tick-Tock development model (Based on [1])
Figure 4.1.1: Intel’s Tick-Tock development model (Based on [1])
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
1. gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
Skylake
New
Microarchi.
14 nm
TOCK
6. gen.

## Slide 73: 3.1 Introduction to the 1. generation Nehalem line (Bloomfield) (2)
Design objective: The same core for all major segments
Figure 3.1.1: Design objective of Nehalem [1]

## Slide 74: 3.1 Introduction to the 1. generation Nehalem line (Bloomfield) (3)
Figure : Overview of Intel’s Tick-Tock model (Based on [3])
New microarch.,
64-bit
New microarch.: 4-wide core,
128-bit SIMD/FP, shared L2 , no HT
11/2007
01/2006
90nm
130nm
TICK TOCK
2 YEARS
2 YEARS
2 YEARS
65nm
TICK Pentium 4 / Cedar Mill
TOCK Core 2
2 YEARS
New microarch.
New microarch.,
hyperthreading (HT)
Pentium 4 /Northwood
TICK TOCK
TICK TOCK
Pentium 4 /Prescott
Pentium 4 /Willamette
07/2006
11/2008
New microarch.: 256-bit AVX,
ring bus, integr. GPU
11/2000
01/2002
02/2004
Key new features of the ISP
and the microarchitecture
The Nehalem line
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
180nm
AVX2,
L4 cache (discrete eDRAM), FIVR
06/2013
09/2014
Shared Virtual Memory
08/2015
ISP,
Memory Side $ (eDRAM), No FIVR
In package integr. GPU
14nm
2 YEARS
TICK Broadwell
TOCK Skylake
New microarch.: integrated MC, QPI,
(inclusive) L3, HT

## Slide 75: 3.1 Introduction to the 1. generation Nehalem line (Bloomfield) (4)
1. generation Nehalem processors
Nehalem lines
Desktops
Servers
DP-Servers
55xx Gainestown (Nehalem-EP) 4C 3/2009
Core i7-9xx (Bloomfield) 4C 11/2008
UP-Servers
35xx Bloomfield 4C 3/2009
Mobiles
1Jasper forest: Embedded UP or DP server
Based on [44]
2. generation Nehalem processors
Desktops
Servers
DP-Servers
C55xx Jasper forest1 2C/4C 2/2010
Core i7-8xx (Lynnfield) 4C 9/2009
Core i5-7xx (Lynnfield) 4C 9/2009
UP-Servers
34xx Lynnfield 4C 9/2009
C35xx Jasper forest1 4C 2/2010
Core i7-9xxM Clarksfield 4C 9/2009
Core i7-8xxQM Clarksfield 4C 9/2009
Core i7-7xxQM Clarksfield 4C 9/2009
Mobiles

## Slide 76: 3.1 Introduction to the 1. generation Nehalem line (Bloomfield) (5)
Die shot of the Bloomfield chip [45]
Die shot of the 1. generation Nehalem desktop processor (Bloomfield) [45]
The Bloomfield die has two QPI bus controllers, in spite of the fact that they are not needed
for the desktop part.
In the Bloomfield die one of the controllers is simply not activated [45], whereas both are
active in the DP alternative (Gainestown).
Both the desktop oriented Bloomfield chip and the DP server oriented Gainestown chip have
the same layout.
Note
(8 MB)

## Slide 77
3.2 Major innovations of the 1. generation Nehalem line
3.2.1 Integrated memory controller
3.2.2 QuickPath Interconnect bus (QPI)
3.2.3 New cache architecture
3.2.5 Enhanced power management
3.2.6 New socket
3.2.4 Simultaneous Multithreading
Notes: 77

## Slide 78: 3.2 Major innovations of the 1. generation Nehalem line (1)
Integrated memory controller
(Section 3.2.1)
QuickPath Interconnect bus (QPI)
(Section 3.2.2)
New cache architecture
(Section 3.2.3)
• Simultaneous Multithreading (SMT)
(Section 3.2.4)
SSE 4.2 ISA extension
(Not detailed)
Enhanced power management
(Section 3.2.5)
Advanced virtualization
(Not detailed)
New socket
(Section 3.2.6)
3.2 Major innovations of the 1. generation Nehalem line [54]
Figure 3.2.1: Die photo of the Bloomfield/Gainestown chip
(8 MB)
The Major incentive for designing the microarchitecture of Nehalem: support of 4 cores.
4 cores need however twice as much bandwidth as dual core processors, such as the Core 2.
Two memory channels used for dual core processors are more or less the limit attachable to
the north bridge due to physical and electrical limitations.
Consequently, to provide enough bandwidth for 4 cores, a new memory design was necessary.
Major innovations of the 1. generation 4-core Nehalem line

## Slide 79: 3.2.1 Integrated memory controller (1)
3.2.1 Integrated memory controller
Example: Dual channel DDR2 memory representing the feasible bandwidth limit for a
dual core Core 2 platform [166]

## Slide 80: 3.2.1 Integrated memory controller (2)
Integrated memory controller in a dual processor Nehalem platform
Main features
3 channels per socket
Up to 3 DIMMs per channel (impl. dependent)
DDR3-800, 1066, 1333,…
Supports both RDIMM and UDIMM (impl. dependent)
Supports single, dual and quad-rank DIMMs
Figure 3.2.1.1: Integrated memory controller of Nehalem [33]
Nehalem-EP (Efficient Performance):
Designation of the server line
More cores
Higher memory bandwidth

## Slide 81: 3.2.1 Integrated memory controller (3)
Benefits and drawback of integrated memory controllers
Low memory access latency
important for memory intensive apps.
Drawback of integrated memory controllers
Processor becomes memory technology dependent
For an enhanced memory solution (e.g. for increased memory speed)
a new processor modification is needed.
Benefits

## Slide 82: 3.2.1 Integrated memory controller (4)
Local memory access
Remote memory access
Most multi-socket platforms use NUMA
Remote memory access latency ~ 1.7 x longer than local memory access latency
Local memory bandwidth is up to 2 x greater than remote bandwidth
Demands a fast processor-to-processor interconnection to relay memory traffic (QPI)
Operating systems have to modify memory allocation strategies + related APIs
Figure 3.2.1.2: Non Uniform Memory Access (NUMA) in multi-socket servers [1]
Non Uniform Memory Access (NUMA)
It is a consequence of using integrated memory controllers in case of multi-socket servers

## Slide 83: 3.2.1 Integrated memory controller (5)
Memory latency comparison: Nehalem vs Penryn
Harpertown: Quad-Core Penryn based server (Xeon 5400 series)
Figure 3.2.1.3: Memory latency comparison: Nehalem vs. Penryn [1]

## Slide 84: 3.2.1 Integrated memory controller (6)
Remark
Intel’s Timna – a forerunner to integrated memory controllers [34]
Timna (announced in 1999, due to 2H 2000, cancelled in Sept. 2000)
Developed in Intel’s Haifa Design and Development Center.
Low cost microprocessor with integrated graphics and memory controller
(for Rambus DRAMs).
Due to design problems and lack of interest from many vendors,
Intel finally cancelled Timna in Sept. 2000.
Figure 3.2.1.4: The low cost (<600 $) Timna PC [40]

## Slide 85: 3.2.1 Integrated memory controller (7)
Point of attaching memory
Attaching memory to the processor(s)
Attaching memory to the MCH
POWER4 (2C) (2001)
POWER5 (2C) (2005)
and subsequent POWER families
Montecito (2C) (2006)
Opteron server lines (2C) (2003)
and all subsequent AMD lines
PA-8800 (2004)
PA-8900 (2005)
and all previous PA lines
Core 2 Duo line (2C) (2006)
and all preceding Intel lines
Core 2 Quad line (2x2C) (2006/2007)
Penryn line (2x2C) (2008)
Figure 3.2.1.5: Point of attaching memory
Nehalem lines (4) (2008)
and all subsequent Intel lines
Examples
Tukwila (4C) (2010)
AMD’s K7 lines (1C) (1999-2003)
UltraSPARC III (2001)
and all subsequent Sun lines
UltraSPARC II (1C) (~1997)

## Slide 86
3.2.2 QuickPath Interconnect bus (QPI)-1
Consists of 2 unidirectional links, one in each directions, called the TX and RX
(T for Transmit, R for Receive).
A serial, high speed differential point-to-point interconnect bus, similar to AMD’s
HyperTransport bus), used to connect processors to processors or processors to north bridges.
Formerly designated as the Common System Interface bus (CSI bus).
3.2.2 QuickPath Interconnect bus (QPI) (1)
Its debut is strongly motivated by the introduction of integrated memory controllers.

## Slide 87
Principle of differential interconnections [170]
3.2.2 QuickPath Interconnect bus (QPI) (2)

## Slide 88
16 data
2 protocol
2 CRC
TX Unidirectional link
RX Unidirectional link
Figure 3.2.4.1: Signals of the QuickPath Interconnect bus (QPI-bus) [22]
Signals of the QuickPath Interconnect bus (QPI bus)
(DDR data transfer)
3.2.2 QuickPath Interconnect bus (QPI) (3)

## Slide 89
QuickPath Interconnect bus (QPI)-2
Each unidirectional link comprises 20 data lanes and a clock lane, with
each lane consisting of a pair of differential signals.
3.2.2 QuickPath Interconnect bus (QPI) (4)
(Lane: Vonalpár)

## Slide 90
Figure: Signaling systems used in buses
LVDS: Low Voltage Differential Signaling LVTTL: Low Voltage TTL
(D)RSL: (Differential) Rambus Signaling Level SSTL: Stub Series Terminated Logic VCM: Common Mode Voltage VREF: Reference Voltage
LVTTL (3.3 V)
FPM/EDO
SDRAM
HI 1.5
TTL (5 V)
FPM/EDO
SSTL
SSTL2 (DDR)
SSTL1.8 (DDR2)
SSTL1.5 (DDR3)
RSL (RDRAM)
FSB
LVDS
PCIe
QPI, DMI, ESI
FB-DIMMs
Smaller voltage swings
DRSL
XDR (data)
Signaling systems used in buses
3.2.2 QuickPath Interconnect bus (QPI) (5)
Signals
Voltage referenced
Single ended
Differential
t
t
VREF
t
S+
S-
VCM
Typ.voltage
swings
600-800 mV
200-300 mV
3.3-5 V
Signaling
system
used in

## Slide 91
QPI based DP and MP server system architectures-1
QPI-based DP system [169]
3.2.2 QuickPath Interconnect bus (QPI) (6)
Note
First generation Nehalem (Bloomfielf) supports only DP configurations.

## Slide 92
QPI based DP and MP server system architectures-2
QPI-based DP system [169]
3.2.2 QuickPath Interconnect bus (QPI) (7)

## Slide 93
QPI-based 8-proc. system [169]
QPI based DP and MP server system architectures-3
3.2.2 QuickPath Interconnect bus (QPI) (8)

## Slide 94
QuickPath Interconnect Bus (QPI-bus)
up to 3.2 GHz DDR 2-Byte (Nehalem)
12.8 GB/s in each direction
Fastest FSB
400 MHz QDR 8 Byte
12.8 GB/s bidirectional
HyperTransport Bus (HT-bus)
HT 1.0: 0.8 GHz DDR 2-Byte
3.2 GB/s in each direction
HT 2.0: 1.0 GHz DDR 2-Byte
4.0 GB/s in each direction
HT 3.0: 2.6 GHz DDR 2-Byte
10.4 GB/s in each direction
Max. clock speed and width figures in AMD’s systems
Comparison of the transfer rates of the QPI, FSB and HT buses
DDR: Double Data Rate
HT 3.1: 3.2 GHz DDR 2-Byte
12.8 GB/s in each direction
QDR: Quad Data Rate
3.2.2 QuickPath Interconnect bus (QPI) (9)
up to 4.0 GHz GHz DDR 2-Byte (Sandy Bridge E/EP)
16.0 GB/s in each direction
up to 4.8 GHz GHz DDR 2-Byte (Haswell E/EP)
19.2 GB/s in each direction

## Slide 95: 3.2.3 New cache architecture (1)
2-level cache hierarchy
(Penryn)
3-level cache hierarchy
(Nehalem)
Figure 3.2.3.1: The 3-level cache architecture of Nehalem (based on [1])
32 kB/32 KB
256 KB
Private
4 MB
Shared/
two cores
Up to 8 MB
Inclusive
3.2.3 New cache architecture
L1 Caches
L1 Caches
L2 Cache
Core
Core
Core
Core
L1 Caches
L2 Cache
Core
32 kB/32 KB
L1 Caches
L1 Caches
L2 Caches
L2 Caches
L3 Cache
Note the difference in the L2 cache sizes.

## Slide 96: 3.2.3 New cache architecture (2)
Distinguished features of Nehalem’s cache architecture
The L2 cache is private again rather than shared as in the Core and Penryn processors
Private L2
Shared L2
Pentium 4
Core
Penryn
Nehalem
Assumed reason for returning to the private scheme
Private caches allow a more effective hardware prefetching than shared ones, since
Hardware prefetchers look for memory access patterns.
Private L2 caches have more easily detectable memory access patterns
than shared L2 caches.

## Slide 97: 3.2.3 New cache architecture (3)
Remark
The POWER family had the same evolution path as above
Private L2
Shared L2
POWER4
POWER5
POWER6

## Slide 98: 3.2.3 New cache architecture (4)
The L3 cache is inclusive rather than exclusive
as in a number of competing designs, such as UltraSPARC IV+ (2005), POWER5 (2005),
POWER6 (2007), POWER7 (2010), AMD’s K10-based processors (2007).
Intel’s argumentation for inclusive caches [38]
Inclusive L3 caches prevent L2 snoop traffic for L3 cache misses since
For higher core numbers L2 snooping becomes a more demanding task
and may overshadow the benefits arising from the more efficient cache use
of the explicit cache scheme.
with inclusive L3 caches an L3 cache miss means that the referenced data
doesn’t exist in any core’s L2 caches, thus no L2 snooping is needed.
By contrast, with exclusive L3 caches the referenced data may exist in any
of the L2 caches, thus L2 snooping is required.

## Slide 99
The notion of “Uncore”
Figure 3.2.3.2: Interpretation of the notion “Uncore” [1]
3.2.3 New cache architecture (5)

## Slide 100: 3.2.4 Simultaneous Multithreading (SMT) (1)
Figure 3.2.4.1: Simultaneous Multithreading (SMT) of Nehalem [1]
3.2.4 Simultaneous Multithreading (SMT)
Two-way multithreaded ( two threads at the same time)
A 4-wide core is fed more efficiently (from 2 threads).
Hides latency of a single tread.
More performance with low additional die area cost,
May provide significant performance increase on
dedicated applications.
Benefits

## Slide 101: 3.2.4 Simultaneous Multithreading (SMT) (2)
Figure 3.2.4.2: Performance gains achieved by Nehalem’ SMT [1]
Performance gains of SMT

## Slide 102: 3.2.5 Enhanced power management (1)
3.2.5 Enhanced power management
Discussed issues
Integrated power gates
Integrated Power Control Unit
Turbo boost technology

## Slide 103: 3.2.5 Enhanced power management (2)
Power switches
Figure 3.2.5.1: Use of integrated power gates [32]

## Slide 104: 3.2.5 Enhanced power management (3)
Allows to manage the power
of the whole chip as an entity.
Used also for the Turbo Boost Mode
Figure 3.2.5.2: Overview of the Power Control unit [32]

## Slide 105: 3.2.5 Enhanced power management (4)
Nehalem’s Turbo Mode
Utilization of the power headroom of inactive cores and that of active cores with light workload
for increasing clock frequency.
1) The Penryn core already introduced a less intricate technology for the same purpose,
termed as the (EDAT) Enhanced Dynamic Acceleration Technology that increases
clock frequency only for the mobile platform and in case of inactive cores.
Remarks
Aim
2) The Turbo Mode technology considers a core “active” if it is in ACPI C0 or C1 states,
whereas cores in the C3 to C6 ACPI states are considered as “inactive”.

## Slide 106: 3.2.5 Enhanced power management (5)
ACPI states [26]
Intelligent
heuristics decides
when enter into.
Passive states

## Slide 107: 3.2.5 Enhanced power management (6)
TDP (Thermal Design Power) is the maximum power consumed at realistic worst case
applications (TDP application) of a processor with a given clock frequency.
The cooling system (thermal solution) needs to be designed for the given TDP.
It has to ensure that the junction temperature (Tj) does not exceed its limit (Tjmax)
while the processor runs TDP applications.
Understanding the notion of TDP and the related potential to boost performance (1) [50]

## Slide 108: 3.2.5 Enhanced power management (7)
Typical workloads however, are not intensive enough to push power consumption to the TDP limit.
The remaining power headroom can be utilized to increase fc.
In principle, the clock frequency can be increased as long as the actual power consumption is
lower than the TDP and also the junction temperature remains below its max. value Tjmax.
Understanding the notion of TDP and the related potential to boost performance (2) [50]

## Slide 109: 3.2.5 Enhanced power management (8)
Principle of the Turbo Boost technology (1) [51]
If the OS requests an active core to increase fc over the max. core frequency that is set
according to the TDP value, but the actual power consumption is less than the TDP, i.e.
there is a power headroom available due to
idle cores or
a light workload
the turbo mode controller will increase the core frequency of the active cores e.g. in steps of
133 MHz, as long as given limits, e.g. the power consumption of the processor (socket) or
the junction temperatures of the cores remain below given limits.
In Nehalem’s turbo mode all active cores in the processor will operate at the same fc and
voltage.
Remarks
When given limits become exceeded the turbo mode controller will step down clock frequency
in steps of 133 MHz.

## Slide 110: 3.2.5 Enhanced power management (9)
Figure 3.2.5.3: Turbo mode uses the available power headroom in processor package power limits [52]
Principle of the turbo boost technology (2) [52]

## Slide 111: 3.2.5 Enhanced power management (10)
Maximum turbo frequencies are factory configured and kept in an internal register (MSR 1ADH).
E.g. in case of the Core i7-920XM the basic core frequency is 2.0 GHz and the maximum
Turbo frequency is 3.2 GHz, which is 9 frequency bins higher than the TDP limited basic
core frequency of 2.0 GHz.
Maximum Turbo boost frequency [53]

## Slide 112: 3.2.5 Enhanced power management (11)
To control fc the turbo boost controller samples the current power consumption and
die temperatures in 5 ms intervals [53].
Power consumption is determined by monitoring the processor current at its input pin as well
as the associated voltage (Vcc) and calculating the power consumption as a moving average.
The junction temperature of the cores are monitored by DTSs (Digital Thermal Sensors) with
an error of ± 5 % [50].
Assuring that power and temperature values do not exceed specified limits [53], [50]
When the power consumption of the processor or the junction temperature of any core
exceeds the factory configured limits, the turbo boost controller automatically steps down
core frequency in increments of e.g. 133 MHz.

## Slide 113: 3.2.6 New sockets (1)
LGA-775
(Core 2)
LGA-1366
(Bloomfied)
LGA-1156
(Lynnfield)
3.2.6 New sockets [167]

## Slide 114
3.3 Major innovations of the 2. generation Nehalem line (Lynnfield)
Notes: 114

## Slide 115: 3.3 Major innovations of the 2. generation Nehalem line (Lynnfield) (1)
1. generation Nehalem processors
Nehalem lines
Desktops
Servers
DP-Servers
55xx Gainestown (Nehalem-EP) 4C 3/2009
Core i7-9xx (Bloomfield) 4C 11/2008
UP-Servers
35xx Bloomfield 4C 3/2009
Mobiles
1Jasper forest: Embedded UP or DP server
Based on [44]
2. generation Nehalem processors
Desktops
Servers
DP-Servers
C55xx Jasper forest1 2C/4C 2/2010
Core i7-8xx (Lynnfield) 4C 9/2009
Core i5-7xx (Lynnfield) 4C 9/2009
UP-Servers
34xx Lynnfield 4C 9/2009
C35xx Jasper forest1 4C 2/2010
Core i7-9xxM Clarksfield 4C 9/2009
Core i7-8xxQM Clarksfield 4C 9/2009
Core i7-7xxQM Clarksfield 4C 9/2009
Mobiles

## Slide 116: 3.3 Major innovations of the 2. generation Nehalem line (Lynnfield) (2)
3.3 Major innovations of the 2. generation Nehalem line (Lynnfield) (1) [46]
a) The Lynnfield chip is a major redesign of the Bloomfield chip resulting in a cheaper and
more effective two-chip system solution instead of the previous three chip solution.
The Bloomfield based platform (X58 + ICH10 / LGA-1366)
The Lynnfield based platform (P55 / LGA-1156)
b) Further on, whereas the Bloomfield chip is connected to the X58 chipset via the QPI bus,
the Lynnfield chip is connected to the P55 PCH by a DMI interface, like in previous solutions.

## Slide 117
Major innovations of the 2. generation Nehalem line (Lynnfield) (2) [46]
The Bloomfield based platform (X58 + ICH10 / LGA-1366)
The Lynnfield based platform (P55 / LGA-1156)
c) It provides only 16 PCIe 2.0 lanes to attach a graphics card immediately to the processor
rather than to the north bridge as done by 36 lanes in the previous solution.
3.3 Major innovations of the 2. generation Nehalem line (Lynnfield) (3)

## Slide 118: 3.3 Major innovations of the 2. generation Nehalem line (Lynnfield) (4)
Evolution of providing PCIe lanes for graphics

## Slide 119
1x x16 or 2x x8 lanes
PCIe lanes provided on the processor
40 configurable lanes
(e.g. 2x x16 + 1x x8 or 4x x8)
PCIe 3.0 lanes
PCIe 2.0 lanes
Type of available PCIe lanes
PCIe 1.0 lanes
Mem.
P
Periph. Contr.
PCIe
2.0
X16/
2x x8
X16/
2x x8
Mem.
P
Periph. Contr.
PCIe
3.0
PCIe 3.0
40
configurable
lanes
Intel 2. gen. Nehalem (Lynnfield) (4C), 2 MCh
with P55 (2009)
Intel Sandy Bridge (4C), 2 MCh with P67 (2011)
Intel Ivy Bridge (4C), 2 MCh with Z77 PCH (2012)
P55/P67
Z77
Intel Ivy Bridge-E (6C), 4 MCh with X79 (2013)
Intel Haswell-E (8C), 4 MCh with X79 (2014)
Main options of providing PCIe lanes on the processor for graphics cards in DT systems
Mem.
P
Periph. Contr.
X79
PCIe 2.0
40
configurable
lanes
Intel Sandy Bridge-E (6C), 4 MCh with X79 (2011)
Mem.
P
Periph. Contr.
X79
3.3 Major innovations of the 2. generation Nehalem line (Lynnfield) (5)
MCh: Memory Channel

## Slide 120: 3.3 Major innovations of the 2. generation Nehalem line (Lynnfield) (6)
PCIe 3.0
lanes
PCIe 2.0
lanes
Type of available PCIe lanes
PCIe 1.0
lanes
Trend
Evolution of the topology and type of available PCIe lanes for graphics cards
Topology of PCIe lanes provided for graphics cards
PCIe lanes
on both the NB and the SB
PCIe lanes
on the NB
PCIe lanes
on the processor
PCIe lanes
on the PCH
2. G. Nehalem (Lynnfield)
(2009)
Sandy Bridge (2011)
Sandy Bridge-E (2011)
Ivy Bridge (2012)
Ivy-Bridge-E (2013)
Haswell-E (2014)
Intel Sandy Bridge E (6C), 4 MCh with X79 (2011)

## Slide 121
d) It supports only two DDR3 memory channels instead of three as in the previous solution.
e) Its socket needs less connections (LGA-1156) than the Bloomfield chip (LGA-1366).
All in all the Lynnfield chip is a cheaper and more effective successor of the Bloomfield chip,
aiming primarily for mobiles and desktops.
Major innovations of the 2. generation Nehalem line (Lynnfield) (3) [46]
The Bloomfield based platform (X58 + ICH10 / LGA-1366)
The Lynnfield based platform (P55 / LGA-1156)
3.3 Major innovations of the 2. generation Nehalem line (Lynnfield) (7)

## Slide 122
Bloomfield
(desktop/DP server) []
Second generation: Lynnfield chip (9/2009) [45]
45 nm, 296 mm2, 774 mtrs, LGA-1156) [45] [46] [48]
First generation: Bloomfield chip (11/2008)
(45 nm, 263 mm2, 731 mtrs, LGA-1366)
Die photos of the 1. and 2. gen.
Nehalem desktop chips
[45], [46], [47]
3.3 Major innovations of the 2. generation Nehalem line (Lynnfield) (8)

## Slide 123
4. The Sandy Bridge line
4.1 Introduction
4.2 Major innovations of the Sandy Bridge line vs.
the 1. generation Nehalem line
4.3 Example for a Sandy Bridge based desktop
platform with the H67 chipset
4.4 The E3-1200 UP microserver line
Notes: 123

## Slide 124
4.1 Introduction
Notes: 124

## Slide 125: 4.1 Introduction (1)
Sandy Bridge is Intel’s next new microarchitecture using 32 nm line width.
First delivered in 1/2011.
It is termed also as Intel’s second generation Core processors.
4.1 Introduction
Figure : Intel’s Tick-Tock development model (Based on [1])
Figure 4.1.1: Intel’s Tick-Tock development model (Based on [1])
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
1. gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
Skylake
New
Microarchi.
14 nm
TOCK
6. gen.

## Slide 126: 4.1 Introduction (2)
Figure : Overview of Intel’s Tick-Tock model (Based on [3])
New microarch.,
64-bit
New microarch.: 4-wide core,
128-bit SIMD/FP, shared L2 , no HT
11/2007
01/2006
90nm
130nm
TICK TOCK
2 YEARS
2 YEARS
2 YEARS
65nm
TICK Pentium 4 / Cedar Mill
TOCK Core 2
2 YEARS
New microarch.
New microarch.,
hyperthreading (HT)
Pentium 4 /Northwood
TICK TOCK
TICK TOCK
Pentium 4 /Prescott
Pentium 4 /Willamette
07/2006
11/2008
New microarch.: 256-bit AVX,
ring bus, integr. GPU
11/2000
01/2002
02/2004
Key new features of the ISP
and the microarchitecture
The Sandy Bridge line
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
180nm
AVX2,
L4 cache (discrete eDRAM), FIVR
06/2013
09/2014
Shared Virtual Memory
08/2015
ISP,
Memory Side $ (eDRAM), No FIVR
In package integr. GPU
14nm
2 YEARS
TICK Broadwell
TOCK Skylake
New microarch.: integrated MC, QPI,
(inclusive) L3, HT

## Slide 127: 4.1 Introduction (3)
Sandy Bridge
Up to 4 cores
(This Section)
Sandy Bridge-E
Up to 6 cores
(Not discussed)
Core i7-3960X EE, 6C, 11/2011
Core i7-3930K, 6C, 11/2011
Core i7-3820, 4C, 11/2011
Desktops
Servers
Mobiles
Core i3-23xxM, 2C, 2/2011
Core i5-24xxM//25xxM, 2C, 2/2011
Core i7-26xxQM/27xxQM/28xxQM, 4C, 1/2011
Core i7 Extreme-29xxXM , 4C, Q1 2011
Core i3-21xx, 2C, 2/2011
Core i5-23xx 4C+G, 1/2011
Core i5/24xx/25xx, 4C+G, 1/2011
Core i7-26xx, 4C+G, 1/2011
Core i7-2700K, 4C+G10/2011
Sandy Bridge-EN/EP
Up to 8 cores
(Not discussed)
Sandy Bridge-EP
(Efficient Performance)
(Socket: LGA 2011)
E5-24xx 4/6/8C, 5/2012
Sandy Bridge-EN
(Entry)
(Socket: LGA 1356)
E5-26xx 4/6/8C, 3/2012
E5-46xx 4/6/8C, 5/2012
DP-Servers
MP-Servers
The Sandy Bridge family
Overview of the Sandy Bridge family
Based on [62] and [63]
Microservers
E3 1220L/1230L/1260L, 2C/4C, 4/2011
UP-Servers
E3 12x0, 4C, 4/2011
E3 12x5, 4C+G, 4/2011
E5-14xx 4/6C, 5/2012
E5-16xx 4/6C, 3/2012
Notes: ridge-ex

## Slide 128: 4.1 Introduction (4)
32K L1D (3 clk)
AVX 256 bit
4 Operands
256 KB L2
(9 clk)
Hyperthreading
AES Instr.
VMX Unrestrict.
20 nm2 / Core
256 KB L2
(9 clk)
256 KB L2
(9 clk)
256 KB L2
(9 clk)
256 KB L2
(9 clk)
256 KB L2
(9 clk)
256 KB L2
(9 clk)
PCIe 2.0
@ 1.0 1.4 GHz
(to L3 connected)
256 b/cycle Ring Architecture
(25 clk)
DDR3-1600
25.6 GB/s
Main functional units of Sandy Bridge [96]
32 nm process / ~225 nm2 die size. 995 mtrs, 85W TDP
8 MB

## Slide 129
4.2 Major innovations of the Sandy Bridge line vs.
the 1. generation Nehalem line
4.2.1 Overview
4.2.2 Extension of the ISA by the 256-bit
AVX instruction set
4.2.3 New microarchitecture of the cores
4.2.4 On die ring interconnect bus
4.2.5 On die graphics unit
4.2.6 Enhanced Turbo Boost technology
Notes: 129

## Slide 130
4.2 Major innovations of the Sandy Bridge line vs. the 2. generation Nehalem line [61]
4.2.1 Overview
4.2.1 Overview (1)
Extension of the ISA by the 256-bit
AVX instruction set (Section 4.2.2)
New microarchitecture for the cores
(Section 4.2.3)
On die ring interconnect bus
(Section 4.2.4)
On-die graphics unit
(Section 4.2.5)
Enhanced Turbo Boost technology
(Section 4.2.6)

## Slide 131
4.2.2 Extension of the ISA by the 256-bit AVX instruction set
4.2.2 Extension of the ISA by the AVX instruction set (1)
AVX: Advanced Vector Extensions
In the course of ISA extensions Intel expanded the previous 128-bit SSE SIMD instruction set (introduced with the Pentium III in 1999) by the 256-bit AVX SIMD instruction set, as follows:

## Slide 132
Width of Intel’s subsequent SIMD extensions (Based on [18])
Norhwood
Northwood (Pentium4)
Northwood (Pentium4)
Ivy Bridge
4.2.2 Extension of the ISA by the AVX instruction set (2)
Pentium III
Pentium III
Core 2
128-bit
64-bit
256-bit

## Slide 133
The 256-bit AVX extension
It includes
Extension of the 128-bit wide XMM [0, 15] SIMD register set to the 256-bit YMM [0, 15]
register set.
b) Extension of the 128-bit SSE instruction set.
4.2.2 Extension of the ISA by the AVX instruction set (3)

## Slide 134
Norhwood
Northwood (Pentium4)
Northwood (Pentium4)
8 MM registers (64-bit),
aliased on the FP Stack registers
8 XMM registers (128-bit)
16 XMM registers (128-bit)
16 YMM registers (256-bit)
Ivy Bridge
4.2.2 Extension of the ISA by the AVX instruction set (4)
Pentium III
Pentium III
Core 2
Available register set
Available SIMD register sets in Intel’s subsequent SIMD extensions (Based on [18])

## Slide 135
Extension of the 128-bit wide XMM [0, 15] SIMD register set to the 256-bit
YMM [0, 15] register set [97], [168]
4.2.2 Extension of the ISA by the AVX instruction set (5)

## Slide 136
b) Extension of the 128-bit SSE instruction set
Supported data types [168]
4.2.2 Extension of the ISA by the AVX instruction set (6)
float
float
FX

## Slide 137
Note
AVX doubled only FP vector width, as indicated in the Figure below [97].
4.2.2 Extension of the ISA by the AVX instruction set (7)
AVX doubled FP vector width
and register file width
Doubling peak FPOPS

## Slide 138
Implementation of AVX -1
To implement 256-bit FP operations Intel did not widen related data paths and FP execution units
to 256 bit, instead designers made use of two 128-bit data paths and two 128-bit
FP execution units in the same time, as indicated in the previous Figure [98].
4.2.2 Extension of the ISA by the AVX instruction set (8)

## Slide 139
Intel redesigned large parts of the microarchitecture of the cores, as indicated by yellow boxes
in the Figure below.
Figure 4.2.2.1: Microarchitecture of the cores of Sandy Bridge [64]
Implementation of AVX -2
4.2.2 Extension of the ISA by the AVX instruction set (9)

## Slide 140
4.2.3 New microarchitectures of the cores (1)
4.2.3 New microarchitecture of the cores
Intel redesigned large parts of the microarchitecture of the cores, as indicated by yellow boxes
in the Figure below.
Figure 4.2.3.1: Microarchitecture of the cores of Sandy Bridge [64]

## Slide 141
Here we do not want to go into details of the microarchitecture, but refer to two very detailed
descriptions [64], [98].
4.2.3 New microarchitectures of the cores (2)

## Slide 142: 4.2.4 On-die ring interconnect bus (1)
4.2.4 On die ring interconnect bus [66]
The ring has six bus stops for
interconnecting
The four cores and the
L3 slices share the same
interfaces.
four cores
four L3 slices
the GPU and
the System Agent
System Agent

## Slide 143: 4.2.4 On-die ring interconnect bus (2)
Main feature of the on-die interconnect bus [64]
• It operates at core frequency (One stop/clock)

## Slide 144: 4.2.5 On die graphics unit (1)
Evolution of graphics implementation from Westmere to Sandy Bridge [99]
4.2.5 On die graphics unit [99]

## Slide 145: 4.2.5 On die graphics unit (2)
Support of both media and graphics processing by the graphics unit [99]

## Slide 146: 4.2.5 On die graphics unit (3)
Main features of the on die graphics unit [99]
12 EUs
8.2.5 On die graphics unit (1)

## Slide 147: 4.2.5 On die graphics unit (4)
Specification data of the HD 2000 and HD 3000 graphics [100]
-
8.2.5 On die graphics unit (1)

## Slide 148: 4.2.5 On die graphics unit (5)
Execution units (EU) of the graphics unit if Sandy Bridge [197]
Each EU is basically a 4-wide SP FP SIMD unit intended to operate on 4-component data
(RGBA), capable of executing 2-operation MAD instructions and also FX instructions.
EUs are 5-way multithreaded for GT2 graphics and 4-way multithreaded for GT1 graphics.
Each thread has a register set of 120 32 B registers.
There is also a fixed function Math Box for executing transcendental, e.g. trigonometric
instructions and also FP divide.
The EUs do not support DP FP operations.
Figure: Block diagram of an EU of the graphics unit of Sandy Bridge
RGBA: RGB Alpha (opacity)

## Slide 149: 4.2.5 On die graphics unit (6)
Remarks
Contrasting the graphics block diagrams of Sandy Bridge and Ivy Bridge [197]

## Slide 150: 4.2.5 On die graphics unit (7)
Sandy Bridge
Ivy Bridge
Comparing the EUs of Sandy Bridge and Ivy Bridge [197]
Note that the EUs of Ivy Bridge
have two 4-wide SP FP units
are 8-way multithreaded
have 128 32 B registers
support DP FP instructions
(at reduced speed)
support FP16 instructions

## Slide 151: 4.2.5 On die graphics unit (8)
Intel’s subsequent graphics EUs
Haswell’s graphics introduced slices beyond sub-slices, else EUs remained more or less unmodified.

## Slide 152: 4.2.5 On die graphics unit (9)
frames per sec
i5/i7 2xxx/3xxx:
Sandy Bridge
i5 6xx
Arrandale
HD 5570
400 ALUs
Performance comparison of the Sandy Bridge’s graphics: gaming [101]

## Slide 153: 4.2.6 Enhanced Turbo Boost technology (1)
Cooler
Designated also as the 2.0 generation Turbo Boost technology.
Thermal capacitance
The concept utilizes the real temperature response of processors to power changes
in order to increase the extent of overclocking [64].
4.2.6 Enhanced Turbo Boost technology [64]

## Slide 154: 4.2.6 Enhanced Turbo Boost technology (2)
Main aspects of Intel’s Turbo Boost Technology 2.0 [198]

## Slide 155
Based on the real temperature response the thermal energy budget accumulated during idle
periods can be utilized to push the core beyond the TDP for short periods of time (e.g. for 20 sec).
Multiple algorithms manage in parallel current, power and die temperature. [64]
4.2.6 Enhanced Turbo Boost technology (3)

## Slide 156
Intelligent power sharing between the cores and the integrated graphics [64]
4.2.6 Enhanced Turbo Boost technology (4)

## Slide 157
[61]
WSM/M
WSM/D
NHM/M
NHM/D
4.2.6 Enhanced Turbo Boost technology (5)

## Slide 158
Remark
Individual cores may run at different frequencies but all cores share the same power plane.
Individual cores may be shut down if idle by power gates.
4.2.6 Enhanced Turbo Boost technology (6)

## Slide 159
4.3 Example for a Sandy Bridge based desktop
platform with the H67 chipset
Notes: 159

## Slide 160: 4.3 Example for a Sandy Bridge based desktop platform with the H67 chipset (1)
4.3 Example for a Sandy Bridge based desktop platform with the H67 chipset [102]

## Slide 161
4.4 The E3-1200 UP microserver line
Notes: 161

## Slide 162: 4.4 The E3-1200 UP microserver line (1)
Intel® Xeon® Processor E3-1200 Product Family Key Features1
Next-Generation 32nm Intel® Microarchitecture
Intel® Turbo Boost 2.0 Technology for dynamic frequency scaling
Intel® Hyper-Threading Technology
Up to 8MB shared L3 cache
Integrated memory controller for 2 channels of DDR3
Up to 32 UDIMMs of memory, up to 1333 MHz of speed
Flexible PCI Express* 2.0 Configurations
Intel® C200 Series Chipset Key Features
New single chip architecture
Up to 8 PCI Express 2.0 x1 Ports (5.0 GT/s)
Up to 2 (6Gb/s) ports plus 4 (3Gb/s) ports with Intel® Rapid Storage Technology for RAID 0/1/5/10
Up to 12 USB 2.0 Ports
1 Not all features are available on every processor SKU
4.4 The E3-1200L UP microserver line [103]

## Slide 163: 4.4 The E3-1200 UP microserver line (2)
Intel’s low power models of the Xeon E3-1200 processor line [175]

## Slide 164
5. The Haswell line
5.1 Introduction
5.2 Major enhancements of the Haswell line vs.
the Sandy Bridge line
5.3 Major innovations of the Haswell line
5.4 Haswell based mobile and desktop processors
5.5 Haswell based microservers
Notes: 164

## Slide 165
5.1 Introduction
Notes: 165

## Slide 166: 5.1 Introduction (1)
Launched: 6/2013 at Computex.
5.1 Introduction
Haswell processors are termed also as the 4. gen. Intel Core processors, as indicated below.
Figure : Intel’s Tick-Tock development model (Based on [1])
Figure 4.1.1: Intel’s Tick-Tock development model (Based on [1])
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
1. gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
Skylake
New
Microarchi.
14 nm
TOCK
6. gen.

## Slide 167: 5.1 Introduction (2)
Figure : Overview of Intel’s Tick-Tock model (Based on [3])
New microarch.,
64-bit
New microarch.: 4-wide core,
128-bit SIMD/FP, shared L2 , no HT
11/2007
01/2006
90nm
130nm
TICK TOCK
2 YEARS
2 YEARS
2 YEARS
65nm
TICK Pentium 4 / Cedar Mill
TOCK Core 2
2 YEARS
New microarch.
New microarch.,
hyperthreading (HT)
Pentium 4 /Northwood
TICK TOCK
TICK TOCK
Pentium 4 /Prescott
Pentium 4 /Willamette
07/2006
11/2008
New microarch.: 256-bit AVX,
ring bus, integr. GPU
11/2000
01/2002
02/2004
Key new features of the ISP
and the microarchitecture
The Haswell line
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
180nm
AVX2,
L4 cache (discrete eDRAM), FIVR
06/2013
09/2014
Shared Virtual Memory
08/2015
ISP,
Memory Side $ (eDRAM), No FIVR
In package integr. GPU
14nm
2 YEARS
TICK Broadwell
TOCK Skylake
New microarch.: integrated MC, QPI,
(inclusive) L3, HT

## Slide 168: 5.1 Introduction (3)
DP/MP servers
They were launched later in 2014, as indicated subsequently.
A second wave of Haswell processors, called the Haswell refresh processors launched in
5/2014.
They do not provide any significant changes vs. the first release processors.
Actually, the manufacturing process could be made more efficient and this resulted in slight
improvements in clock speeds.
Haswell refresh processors [176]

## Slide 169: 5.1 Introduction (4)
Desktops (2-chip designs)
Servers
Overview of the Haswell family-1
Core i7-49xx/48xx/472x/471x/470x, 4C+G, HT, 6/2013 and 5/2014
Core i7-46xx/45xx, 2C+G, HT, 5/2013 and 6/2014
Core i5-43xx/42xx U/Y, 2C+G, HT, 6/2013 and 5/2014
Core i3-41xx/40xx, 2C+G, HT, 6/2013 and 5/2014
Core i7-479x/478x/477x,476x, 4C+G, HT, 6/2013 and 5/2014
Core i5-46xx/45xx/44xx, 4C+G, HT, 6/2013 and 5/2014
Core i3-43xx/41xx, 2C+G, HT, 6/2013, 5/2014 and 3/2015
i7-5960X/5930K/5820K, 6/8 C, 8/2014
(See next slide)
Haswell
(LGA1150)
Up to 4 cores
(This Section)
Haswell-E
(LGA2011)
Up to 8 cores
(Not discussed here)
The Haswell family
Haswell-EP
(LGA2011)
Up to 18 cores
(Not discussed ere)
Haswell-EX
(LG2011)
Up to 18 cores
(Not discussed here)
Mobiles (SoCs)
Notes: ridge-ex

## Slide 170: 5.1 Introduction (5)
M – mobile processor (Socket G3)
Q – quad-core
U – ultra-low power (BGA1168 packaging)
X – "extreme"
Y – extreme low-power (BGA1168 packaging)
E / H – BGA1364 packaging
K – unlocked (adjustable CPU multiplier up to 63x)
S – performance-optimized lifestyle (low power with 65 W TDP)
T – power-optimized lifestyle (ultra low power with 35–45 W TDP)
R – BGA packaging / High-performance GPU (currently Iris Pro 5200 (GT3e))
X – extreme performance (adjustable CPU ratio with no ratio limit)
Interpretation of the mobile suffixes
Interpretation of the desktop suffixes
Interpretation of the model suffixes [205]

## Slide 171: 5.1 Introduction (6)
Haswell
(LGA1150)
Up to 4 cores
(This Section)
Haswell-E
(LGA2011)
Up to 8 cores
(Not discussed here)
The Haswell family
Haswell-EP
(LGA2011)
Up to 18 cores
(Not discussed ere)
Haswell-EX
(LG2011)
Up to 18 cores
(Not discussed here)
Servers
Microservers
E3-1275L/1265L v3, 4C+G, HT, 6/2013 and 5/2014
E3-1240L/1230L/1220L v3, 2C/4C, HT, 6/2013 and 5/2014
UP Servers
E3-12x5/12x6 v3, 4C+G, HT, 6/2013 and 5/2014
E3-12x0/12x1 v3, 4C, HT, 6/2013 and 5/2014
E5-16xx v3, 4/6/8, 9/2014
Workstations
DP-Servers
MP-Servers
E5-26xx v3, 4/6/8/10/12/14/16/18C, 9/2014
E5-46xx v3, 6/10/12/14/16/18C, 6/2015
E7-48xx v3, 8/10/12/14, 5/2015
E7-88xx v3, 4/10/16/18C, 5/2015
Overview of the Haswell family-2

## Slide 172: 5.1 Introduction (7)
Note
Mobiles, desktops, microservers and UP servers include two or four cores, whereas
workstations, DP and MP servers typically more, up to 18 cores, as indicated in the
above overviews.

## Slide 173: 5.1 Introduction (7)
Die plot of a quad core Haswell processor [121]

## Slide 174: 5.1 Introduction (9)
Die plot of a dual core Haswell processor [177]

## Slide 175: 5.1 Introduction (10)
[204]

## Slide 176: 5.1 Introduction (11)
Single thread IPC in Intel’s basic architectures [195]
20%
18%
16%
14%
12%
10%
8%
6%
4%
2%
0%
1.8
1.7
1.6
1.5
1.4
1.3
1.1
1.2
1
Per Generation
Cumulative
Pentium M
Dothan
Core 2
Penryn
NHM (w/o SMT)
WSM
SNB
IVB
HSW
BRW

## Slide 177
5.2 Major enhancements of the Haswell line vs.
the Sandy Bridge line
5.2.1 Overview
5.2.3 Enhanced microarchitecture for the cores
5.2.4 Enhanced graphics
5.2.2 ISA extension (of the cores) by the AVX2
instruction set
Notes: 177

## Slide 178: 5.2.1 Overview (1)
5.2 Major enhanchements of the Haswell line vs. the Sandy Bridge line
5.2.1 Overview
ISA extension by the AVX2
instruction set (Section 5.2.2)
Enhanced microarchitecture for the cores
(Section 5.2.3)
Enhanced graphics (Section 5.2.4)

## Slide 179: 5.2.2 ISA extension by the AVX2 instruction set (1)
5.2.2 ISA extension by the AVX2 instruction set -1 [97]

## Slide 180: 5.2.2 ISA extension by the AVX2 instruction set (2)
ISA extension by the AVX2 instruction set -2 [80]

## Slide 181: 5.2.2 ISA extension by the AVX2 instruction set (3)
Evolution of the AVX ISA extensions [97]

## Slide 182: 5.2.2 ISA extension by the AVX2 instruction set (4)
Expected future evolution of AVX [165]

## Slide 183: 5.2.3 Enhanced microarchitecture for the cores (1)
5.2.3 Enhanced microarchitecture for the cores [80]

## Slide 184: 5.2.3 Enhanced microarchitecture for the cores (2)
Buffer sizes of subsequent generations of the Core processors [80]

## Slide 185: 5.2.3 Enhanced microarchitecture for the cores (3)
Cache sizes, latencies and bandwidth values of subsequent Core generations [122]

## Slide 186: 5.2.3 Enhanced microarchitecture for the cores (4)
Issue rate and execution unit enhancements of Haswell [165]
FMA: Fused Multiply-Add (a x b+c)

## Slide 187
5.2.4 Enhanced graphics (1)
5.2.4 Enhanced graphics
To compete with AMD’s advanced graphics solutions Intel put a great emphasis on enhancing
Haswell’s integrated graphics.
Main features of the new graphics units: are termed as Iris Pro and Iris graphics.
Sliced graphics architecture to allow scaling of EUs
Inclusion of eDRAM in high-end units.

## Slide 188: 5.2.4 Enhanced graphics (2)
a) Introduction of sliced graphics architecture
The new graphics architecture of Haswell is sliced, to allow scaling of EUs by using one or two slices/unit.
Each slice has two sub-slices, with up to 10 EUs/sub-slice, as indicated in the Figure below.
Figure: A sub-slice with 10 EUs
of the graphics unit of Haswell [199]

## Slide 189: 5.2.4 Enhanced graphics (3)
A slice of the graphics unit of Haswell including two sub-slices with 20 Eus [199]

## Slide 190: 5.2.4 Enhanced graphics (4)
The architecture of a GT3 graphics unit of Haswell including two slices with 40 EUs [199]

## Slide 191: 5.2.4 Enhanced graphics (5)
Block diagram of an EU of Haswell -1 [199]
Each EU has four functional units:
Two 4-way SIMD FPU units
1 Send unit (Load/Store) and
1 Branch unit.
An EU issues up to 4 instructions per cycle to the functional units.

## Slide 192: 5.2.4 Enhanced graphics (6)
Block diagram of an EU of Haswell -2 [199]
Each SIMD FPUs can execute 4 SP FP or 1/2/4/8/16/32 bit wide FX operations.
They can execute MAD instructions (Multiply-Add) per cycle.
Thus an EU can execute 2 FPU x SIMD4 x 2 (MAD) = 16 SP FP operations/cycle.
The EU is 7-way multithreaded.
Each thread has 128 32 B registers.
One of the FPUs also supports FX operations.
One of the FPUs also support transcendental math functions.

## Slide 193: 5.2.4 Enhanced graphics (7)
Interpretation of the notions Graphics Technology (GT) for the Haswell line and
subsequent lines
GT1 designates graphics with a single slice and reduces execution resources (less sub-slices
or less EUs per sub-slice)
GT2 designates graphics with a single slice
GT3 designates graphics with dual slices
GT4 designates graphics with triple slices.

## Slide 194: 5.2.4 Enhanced graphics (8)
Introducing the notions Iris/Iris Pro graphics
Intel designates their
high-end graphics as Iris graphics and
high-end graphics enhanced with embedded DRAM (eDRAM) as Iris Pro graphics.
The inclusion of eDRAM will be indicated also in the GT naming by supplementing the GT level
by the letter “e”, so GT3e designates GT3 level with eDRAM.
Iris graphics unit
Iris Pro graphics unit
Haswell’s Iris graphics unit
(They incorporate two slices with altogether 40 EUs
It is enhanced by a 128 MB sized
on package integrated eDRAM
It is not enhanced by an
on package integrated eDRAM

## Slide 195: 5.2.4 Enhanced graphics (9)
b)Inclusion of eDRAM in high-end graphics units
It will be discussed in Section 5.3.1

## Slide 196: 5.2.4 Enhanced graphics (10)
Intel Core generation | Graphics generation | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Westmere | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 7th | HD 2500 | GT1 | 1 (6 EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 8th | HD 5300- HD 5600 | GT2 | 1(3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Evolution of main features of Intel’s graphics families

## Slide 197: 5.2.4 Enhanced graphics (11)
Haswell
Sandy Bridge
Ivy Bridge
Graphics performance increase of subsequent Core generations [117]

## Slide 198
5.3 Major innovations of the Haswell line
5.3.1 On-package eDRAM cache
5.3.2 FIVR (Fully Integrated Voltage Regulator)
Notes: 198

## Slide 199: 5.3 Major innovations of the Haswell line (1)
5.3 Major innovations of the Haswell line
On-package e-DRAM cache (Section 5.3.1)
FIVR (Fully Integrated Voltage Regulator) (Section 5.3.2)

## Slide 200: 5.3.1 On-package eDRAM cache (1)
5.3.1 On-package eDRAM cache [117]

## Slide 201: 5.3.1 On-package eDRAM cache (2)
Principle of operation [117]
The on package eDRAM, designated also as Crystallwell, it operates as a true 4th level cache
of the memory hierarchy.
It acts as a victim buffer to the L3 cache, in the sense that anything evicted from the
L3 cache immediately goes into the L4 cache.
Both CPU and GPU requests are cached.
The cache partitioning between CPU and GPU is dynamic.
If the GPU is not in use the whole L4 cache may be devoted the CPU, in this case the CPU
has a 128 MB L4 cache.
Access latency after an L3 miss is 30 – 32 ns.
The L4 cache is capable of delivering 50 GB/s in each direction.
The Crystallwell die consumes between 0.5 and 1.0 W if idle and between 3.5 and 4.5 W
under full load.
The PCU (Power Control Unit) of the processor takes over the power management of the
eDRAM, beyond the power management of the CPU cores, GPU, L3 cache etc.

## Slide 202: 5.3.1 On-package eDRAM cache (3)
Implemented on-package eDRAM [124]
eDRAM chip

## Slide 203: 5.3.1 On-package eDRAM cache (4)
L1
L2
L3
L4
Memory
Memory latency vs. access range in a memory system with eDRAM cache (L4) [117]
Ivy Bridge
Ivy Haswel with Chrystallwelll
Ivy Haswell without CRW

## Slide 204: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (1)
Voltage planes in desktop and mobile Haswell processors [173]
5.3.2 FIVR (Fully Integrated Voltage Regulator)

## Slide 205: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (2)
Implementation of the voltage planes in Ivy Bridge and Haswell platforms [149]

## Slide 206: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (3)
Functional partitioning of Haswell’s FIVR implementation [150]
Functional partitioning
The first stage of the voltage regulator converts
from the PSU or battery voltage (12V)
to approximately 1.8V, which is distributed
across the microprocessor die.
The second conversion stage is comprised of
between 8 and 31 (depending on the
product) FIVRs, which are 140MHz
synchronous multiphase buck converters
with up to 16 phases.
FIVR is built up of two stages.
12 V
First stage
Second stage

## Slide 207: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (4)
Partitioning of the implementation [150]
The first stage is on the
motherboard.
The inductors and the midfrequency decoupling capacitors are placed on the package.
The power FETs, control circuitry and high frequency decoupling are on the die.
Each FIVR is independently programmable to achieve optimal operation given the requirements of the domain it is powering.
The settings are optimized by the Power Control Unit (PCU), which specifies the input voltage, output voltage, number of operating phases, and a variety of other settings to minimize the total power consumption of the die.

## Slide 208: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (5)
Figure: Block diagram of the Buck converter [151]
Principle of operation of the Buck converter [151]
On state
Off state
Figure: Operation of the Buck converter [151]
Q: MOSFET
Drive circuit:
E.g. PWM modulated
(Pulse Width Modulated)

## Slide 209: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (6)
Fig. 9: Principle of a synchronous n-phase buck converter [152]
Enhancing the buck converter to synchronous n-phase buck design to reduce ripple [152]

## Slide 210: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (7)
Simplified block diagram of a single voltage plane in the FIVR domain of Haswell [150]

## Slide 211: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (8)
Board space saving with Haswell’s FIVR vs. Ivy Bridge’s voltage regulator [149]

## Slide 212: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (9)
Remark [171]
The availability of the FIVR solution allows a per-core P-state control of the
clock frequency and core voltage.
Despite this possibility only the server/workstation class processors make use
of this feature in the Haswell family, but desktop or mobile focused products no.

## Slide 213: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (10)
Per Core P-State (PCPS) management in Intel’s i5-2600v3 (Haswell-EP) [172]

## Slide 214: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (11)
Assessment of FIVR
Benefits of FIVR [178]

## Slide 215: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (12)
Drawbacks of FIVR [178]
Hot running FIVR increases die temperature and thus it has a limiting effect on overclcking.
As a consequence, after using FIVR in Broadwell, Intel decided to remove it in their upcoming
Skylake and Kaby Lake processors.
Accordingly, related motherboards need to provide appropriate power delivery.
Nevertheless, sources state that in the subsequent 10 nm Cannonlake processors, due to
in 2017, Intel will make use again of the FIVR technology probably to achieve higher CPU
efficiency or due to the fact that thermal issues could be amended.

## Slide 216: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (13)
In their subsequent Broadwell family (2014) Intel introduced the 2nd generation FIVR with 3DL
design [155]
3DL: 3D Layering
Remark

## Slide 217
5.4 Haswell based mobile and desktop processors
Notes: 217

## Slide 218: 5.4 Haswell based mobile and desktop processors (1)
Desktops (2 chips)
Servers
5.4 Haswell based mobile and desktop processors
Core i7-49xx/48xx/472x/471x/470x, 4C+G, HT, 6/2013 and 5/2014
Core i7-46xx/45xx, 2C+G, HT, 5/2013 and 6/2014
Core i5-43xx/42xx U/Y, 2C+G, HT, 6/2013 and 5/2014
Core i3-41xx/40xx, 2C+G, HT, 6/2013 and 5/2014
Core i7-479x/478x/477x,476x, 4C+G, HT, 6/2013 and 5/2014
Core i5-46xx/45xx/44xx, 4C+G, HT, 6/2013 and 5/2014
Core i3-43xx/41xx, 2C+G, HT, 6/2013, 5/2014 and 3/2015
i7-5960X/5930K/5820K, 6/8 C, 8/2014
(See next slide)
Haswell
(LGA 1150)
Up to 4 cores
(This Section)
Haswell-E
(LGA 2011)
Up to 8 cores
(Not discussed here)
The Haswell family
Haswell-EP
(LGA 2011)
Up to 18 cores
(Not discussed ere)
Haswell-EX
(LGA 2011)
Up to 18 cores
(Not discussed here)
Mobiles (SoCs)
Notes: ridge-ex

## Slide 219
Intel 4th Gen Core i7 M-Series Mobile Processors |  |  |  |  | 
Model | Core i7-4930MX | Core i7-4900MQ | Core i7-4800MQ | Core i7-4702MQ | Core i7-4700MQ
Cores/Threads | 4/8 | 4/8 | 4/8 | 4/8 | 4/8
CPU Base Freq | 3.0 | 2.8 | 2.7 | 2.2 | 2.4
Max SC Turbo | 3.9 | 3.8 | 3.7 | 3.2 | 3.4
Max DC Turbo | 3.8 | 3.7 | 3.6 | 3.1 | 3.3
Max QC Turbo | 3.7 | 3.6 | 3.5 | 2.9 | 3.2
TDP | 57W | 47W | 47W | 37W | 47W
HD Graphics | 4600 | 4600 | 4600 | 4600 | 4600
GPU Clock | 400-1350 | 400-1300 | 400-1300 | 400-1150 | 400-1150
L3 Cache | 8MB | 8MB | 6MB | 6MB | 6MB
DDR3/DDR3L | 1600 | 1600 | 1600 | 1600 | 1600
vPro/TXT/VT-d | Yes | Yes | Yes | No | No
Intel SBA | No | No | No | Yes | Yes
Price | $1096 | $568 | $378 |  | 
Main features of first introduced Haswell-based mobile Core i7 M-Series processors [125]
5.4 Haswell based mobile and desktop processors (2)

## Slide 220
Intel 4th Gen Core i7 Desktop Processors |  |  |  |  |  | 
Model | Core i7-4770K | Core i7-4770 | Core i7-4770S | Core i7-4770T | Core i7-4770R | Core i7-4765T
Cores/Threads | 4/8 | 4/8 | 4/8 | 4/8 | 4/8 | 4/8
CPU Base Freq | 3.5 | 3.4 | 3.1 | 2.5 | 3.2 | 2.0
Max Turbo | 3.9 (Unlocked) | 3.9 | 3.9 | 3.7 | 3.9 | 3.0
Test TDP | 84W | 84W | 65W | 45W | 65W | 35W
HD Graphics | 4600 | 4600 | 4600 | 4600 | Iris Pro 5200 | 4600
GPU Max Clock | 1250 | 1200 | 1200 | 1200 | 1300 | 1200
L3 Cache | 8MB | 8MB | 8MB | 8MB | 6MB | 8MB
DDR3 Support | 1333/1600 | 1333/1600 | 1333/1600 | 1333/1600 | 1333/1600 | 1333/1600
vPro/TXT/VT-d/SIPP | No | Yes | Yes | Yes | No | Yes
Package | LGA-1150 | LGA-1150 | LGA-1150 | LGA-1150 | BGA | LGA-1150
Price | $339 | $303 | $303 | $303 |  | $303
Main features of first issued Haswell-based Core i7 desktop processors [126]
5.4 Haswell based mobile and desktop processors (3)

## Slide 221
Example of a Haswell-based desktop platform [145]
5.4 Haswell based mobile and desktop processors (4)

## Slide 222
Integer and FP performance of subsequent generations of desktop processors [127]
Sandy Bridge
Ivy Bridge
Haswell
5.4 Haswell based mobile and desktop processors (5)

## Slide 223
Note
As the AVX2 extension of the Haswell processors introduces 256-bit FX operations, this line
has a considerable higher integer performance than previous Core generations.
5.4 Haswell based mobile and desktop processors (6)

## Slide 224
Graphics performance of subsequent generations of desktop processors [127]
Sandy Bridge
Ivy Bridge
Haswell
5.4 Haswell based mobile and desktop processors (7)

## Slide 225
5.5 Haswell based microservers
Notes: 225

## Slide 226: 5.5 Haswell-based microservers (1)
Haswell
(LGA1150)
Up to 4 cores
(This Section)
Haswell-E
(LGA2011)
Up to 8 cores
(Not discussed here)
The Haswell family
Haswell-EP
(LGA2011)
Up to 18 cores
(Not discussed ere)
Haswell-EX
(LG2011)
Up to 18 cores
(Not discussed here)
Servers
Microservers
E3-1275L/1265L v3, 4C+G, HT, 6/2013 and 5/2014
E3-1240L/1230L/1220L v3, 2C/4C, HT, 6/2013 and 5/2014
UP Servers
E3-12x5/12x6 v3, 4C+G, HT, 6/2013 and 5/2014
E3-12x0/12x1 v3, 4C, HT, 6/2013 and 5/2014
E5-16xx v3, 4/6/8, 9/2014
Workstations
DP-Servers
MP-Servers
E5-26xx v3, 4/6/8/10/12/14/16/18C, 9/2014
E5-46xx v3, 6/10/12/14/16/18C, 6/2015
E7-48xx v3, 8/10/12/14, 5/2015
E7-88xx v3, 4/10/16/18C, 5/2015
5.5 Haswell-based microservers [147]

## Slide 227: 5.5 Haswell-based microservers (2)
Main features of first issued Haswell-based Xeon E3-12xx v3 microservers [147]

## Slide 228: 5.5 Haswell-based microservers (3)
Main features of subsequent generations of E3-1200 Xeon microserver processors [129]
V1: Sandy Bridge V2: Ivy Bridge V3: Haswell

## Slide 229: 5.5 Haswell-based microservers (4)
Example for a Haswell-based Xeon E3-1200 v3 microserver platform
(Called the Denlow platform) [130]

## Slide 230
6. The Skylake line
6.1 Introduction
6.2 Major enhancements of the Skylake line vs.
the Broadwell line
6.3 Major innovations of the Skylake line
6.4 Skylake based processor lines
Notes: 230

## Slide 231
6.1 Introduction
Notes: 231

## Slide 232: 6.1 Introduction (1)
5.1 Introduction (1)
6.1 Introduction
Skylake processors are termed also as the 6. gen. Intel Core processors, as indicated below.
Figure : Intel’s Tick-Tock development model (Based on [1])
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
1. gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
Skylake
New
Microarchi.
14 nm
TOCK
6. gen.
The Skylake line is built on 14 nm technology.
Launched: 08/2015

## Slide 233: 6.1 Introduction (2)
Figure : Overview of Intel’s Tick-Tock model (Based on [3])
New microarch.,
64-bit
New microarch., 4-wide core,
128-bit SIMD, no hyperthreading
11/2007
01/2006
90nm
130nm
TICK TOCK
2 YEARS
2 YEARS
2 YEARS
65nm
TICK Pentium 4 / Cedar Mill
TOCK Core 2
2 YEARS
New microarch.
New microarch.,
hyperthreading
Pentium 4 /Northwood
TICK TOCK
TICK TOCK
Pentium 4 /Prescott
Pentium 4 /Willamette
07/2006
11/2008
256-bit AVX, new microarch.,
ring bus, integr. GPU
11/2000
01/2002
02/2004
The Skylake line
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
180nm
AVX2,
L4 cache (discrete eDRAM), FIVR
06/2013
09/2014
Shared Virtual Memory
08/2015
ISP,
Memory Side $ (eDRAM), No FIVR
In package integr. GPU
14nm
2 YEARS
TICK Broadwell
TOCK Skylake
Key new features of the ISP
and the microarchitecture
New microarch., integrated MC, QPI,
(inclusive) L3, hyperthreading

## Slide 234: 6.1 Introduction (3)
According to sources quoting Intel’s statements [] on average, Skylake has 10% better
performance, 30% better graphics performance.
http://gizmodo.com/intels-new-skylake-processors-what-you-need-to-know-1728020921
Performance improvements provided by Skylake

## Slide 235: 6.1 Introduction (4)
Per Generation
Cumulative
Pentium M Dothan
Core 2
Penryn
NHM (w/o SMT)
WSM
SNB
IVB
HSW
BRW
1.8
1.7
1.6
1.5
1.4
1.3
1.1
1.2
1
2
1.9
20%
18%
16%
14%
12%
10%
8%
6%
4%
2%
0%
24%
22%
SKL
Single thread IPC in Intel’s basic architectures (Based on [195])
Note that Intel raised IPC in the Core family only less then 2-times in about 10 years.

## Slide 236: 6.1 Introduction (5)
http://gizmodo.com/intels-new-skylake-processors-what-you-need-to-know-1728020921
4.5 W
15/28 W
45 W
65/91 W
Skylake Series -1 []

## Slide 237: 6.1 Introduction (6)
http://gizmodo.com/intels-new-skylake-processors-what-you-need-to-know-1728020921
Skylake Series -2 []

## Slide 238: 6.1 Introduction (7)
This diagram shows a kind of "superset" of Skylake. Different versions will not include all
of these parts, but these are all the different components that can be included.
Main enhancements and innovations of Intel’s Skylake microarchitecture [200]

## Slide 239
6.2 Major enhancements of the Skylake line
6.2.1 More advanced microarchitecture of the cores
6.2.2 Enhanced graphics
Notes: 239

## Slide 240: 6.2 Major enhancements of the Skylake line
6.2 Major enhancements of the Skylake line
6.2.1 More advanced microarchitecture of the cores

## Slide 241: 6.2.1 More advanced microarchitecture of the cores (1)
Instruction window (ROB), buffer and register sizes of subsequent generations of the
Core 2 family [200]

## Slide 242: 6.2.2 Enhanced graphics (1)
Skylake
Broadwell
Haswell
Ivy Bridge
Sandy Bridge
6.2.2 Enhanced graphics
Performance increase of Intel’s graphics over generations [196]

## Slide 243: 6.2.2 Enhanced graphics (2)
Intel Core generation | Graphics generation | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Westmere | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 7th | HD 2500 | GT1 | 1 (6 EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  | HD 530 | GT2 | 1 | 24 |  |  |  | 
 |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Evolution of main features of Intel’s graphics families

## Slide 244: 6.2.2 Enhanced graphics (3)
Expected main features of the Skylake line [190]

## Slide 245: 6.2.2 Enhanced graphics (4)
Skylake/Gen9 graphics architecture overview [196]

## Slide 246: 6.2.2 Enhanced graphics (5)
Gen9 graphics scalability -1 [196]

## Slide 247: 6.2.2 Enhanced graphics (6)
Gen9 graphics scalability -2 [196]

## Slide 248: 6.2.2 Enhanced graphics (7)
Scaling for GT 1.5 to reduce power
Gen9 graphics scalability -3 [196]

## Slide 249: 6.2.2 Enhanced graphics (8)
Gen9 graphics Codec support [196], [201]
With the new hardware accelerated codec solution watching a movie or video conferencing
can be done by highly efficient fixed-function circuits rather than by using more flexible, but
more power hungry CPU and GPU cores [201]

## Slide 250: 6.2.2 Enhanced graphics (9)
SPCS003 IDF15 San Francisco Aug. 2015
Gen9 graphics display support [201]
It supports 3 display pipes.
WiDi is Intel’s Wireless Display technology to transmit music, videos, movies, photos etc.
from a WiDi compatible computer to a compatible HDTV.
The initial version of WiDi supported only a low resolution of 720p, Skylake provides already
HD quality with a resolution of 1080.
Miracast is a WiDi standard of the Wi-Fi Alliance providing HD quality.

## Slide 251: 6.2.2 Enhanced graphics (10)
Note
Skylake does not make use of the FIVR technology, as indicated in the Figure below.
The reason for omitting FIVR in Skylake (and probably also is the subsequent Cannonlake) is
that it increases unduly the die temperature and limits overclocking.
Figure: Voltage domains of Skylake [200]
Note that all cores share the same voltage
and even the same frequency.

## Slide 252
6.3 Major innovations of the Skylake line
6.3.1 Integrated ISP (Image Signal Processing)
6.3.2 Memory Side Cache
6.3.3 Innovations in power management
Notes: 252

## Slide 253: 6.3.1 Integrated ISP (Image Signal Processing) (1)
6.3 Major innovations of the Skylake line
6.3.1 Integrated ISP (Image Signal Processing) [200]

## Slide 254: 6.3.2 Memory Side Cache (MSC) (1)
The eDRAM cache of Broadwell [200]
6.3.2 Memory Side Cache (MSC)
Note: The L4 eDRAM cache operates as a victim cache to the L3 (LLC).

## Slide 255: 6.3.2 Memory Side Cache (MSC) (2)
MS$: Memory Side Cache
Memory Side Cache of the Skylake [200]

## Slide 256: 6.3.2 Memory Side Cache (MSC) (3)
Benefits of the Memory Side Cache (MSC) [200]
It is fully coherent.
It can cache any data including “uncacheable memory” types.
No need to flush it for coherency maintenance.
Available for use by I/O devices and the Display engine as well.
For optimal performance GFX driver may choose caching of particular data in the eDRAM only and not in the LLC.

## Slide 257: 6.3.3 Innovations in power management
6.3.3 Innovations in power management
6.3.3.1 Speed Shift Technology
6.3.3.2 Duty cycle control of the cores

## Slide 258: 6.3.3.1 Speed Shift Technology (1)
6.3.3.1 Speed Shift Technology [198]
The legacy power management technology, called the DVFS (Dynamic Voltage and
Frequency Scaling).
Intel’s DVFS implementation is termed as the SpeedStep
technology.
It is demand based, i.e. first the OS determines the actual
core or processor utilization based on the current workload,
then it selects the appropriate working point, called P point,
of the core or of the processor.
Each Pi point is set up of the operating {fci, Vci} values.
The OS selects the appropriate Pi point from the given set of
available Pi points (from the P1 point, associated with
the highest guaranteed clock frequency and the Pn point,
associated with the min. clock frequency (see the Figure),
while taking into account both the workload demand and
the user specified power management policy that specifies
the user’s power management priority (such as max.
performance, longest battery life or balanced).
The selected fci/Vci value will be communicated to the
hardware (PLL, voltage regulator).
On the other hand, when the workload demands a higher
operating point than P1, the processor can take over the
control over the power management by activating the
turbo technology.
Lower than Pn states are used only to manage critical
conditions, like overheating the die.

## Slide 259: 6.3.3.1 Speed Shift Technology (2)
The drawback of the SpeedStep technology
The basic drawback is slow responsiveness, e.g. 30 ms responsiveness, needed until the OS
recognizes the change of operating conditions (e.g. workload) and responds by resetting the
operating point [201].
This is unfavorable for low residency workloads, like quickly changing video recording.

## Slide 260: 6.3.3.1 Speed Shift Technology (3)
Principle of the Speed Shift Technology
The OS passes the control over power management to the processor, more precisely to the
PCU (Power Control Unit) of the processor, along with hints about the user preference
concerning power management (like max. performance, max. battery life etc.).
The PCU performs the actual P-state control, called the Autonomous Control.
The Autonomous control can cover all p-states or a subset of the P-states, as indicated in the
next Figures.

## Slide 261: 6.3.3.1 Speed Shift Technology (4)
Passing power management control for all P-states to the CPU [198]

## Slide 262: 6.3.3.1 Speed Shift Technology (5)
Passing power management control for a subset of P-states to the CPU [198]

## Slide 263: 6.3.3.1 Speed Shift Technology (6)
Benefit of the Speed Shift Technology
It reduces the responsiveness of the power management from 30 ms to about 1 ms [201].

## Slide 264: 6.3.3.2 Duty cycle control (1)
While running applications
dynamic dissipation: ~ f3
runtime: ~ 1/f
total energy consumption originating from the dynamic dissipation: ~ f2
with f denoting the clock frequency.
As the performance ~ f, the energy consumption originating from the dynamic dissipation
depends on the performance as shown below.
Figure: Dependence of energy consumption originating from the dynamic dissipation
(designated as Compute energy in the Figure) on the performance (~ f)
6.3.3.2 Duty cycle control [198]

## Slide 265: 6.3.3.2 Duty cycle control (2)
On the other hand
the total energy consumption originating from static dissipation and system power depends
on the runtime, i.e.
the total energy consumption originating from static dissipation and system power: 1/f,
as indicated in the Figure below.
Figure: Dependence of energy consumption originating from the static dissipation
and system power (designated as SoC and system energy in the Figure) on the performance (~ f) [198]

## Slide 266: 6.3.3.2 Duty cycle control (3)
As a consequence, the total energy consumption originating from both the
dynamic dissipation and
static dissipation as well as system power consumption
has a minimum, as indicated in the Figure below.
Figure: Dependence of energy consumption originating from both the dynamic dissipation (designated as the Compute energy in the Figure) and the static dissipation and system power (designated as SoC and system energy in the Figure) on the performance
Obviously, the min. energy consumption point (Pe) is the most efficient working point of a core
of the processor.

## Slide 267: 6.3.3.2 Duty cycle control (4)
Power management with taking into account the most efficient Pe working point [198]
Frequency will be lowered as far as possible until the Pe working point is reached.
Pe will be calculated every ms based on the workload and system characteristics.
There is no benefit when the system is clocked below the Pe point, as it would increase
the energy consumption.
Therefore, a so called EARtH algoritm overrides lower P requests and sets f according to Pe.
The EARtH algorithm is activated only if it is possible to enter the package sleep state.
Figure: Power management with taking into account the most efficient Pe working point [198]

## Slide 268: 6.3.3.2 Duty cycle control (5)
Duty cycling [198]
While managing power going below Pe would reduce energy consumption inefficiently
due to the fixed power components.
In this region turning the package on and off, called duty cycling, reduces power
proportionally to run time, as shown in the Figure below.
Duty cycling is more effective technique to reduce power for low computing demand in the
region below Pe than reducing frequency below the value associated with Pe..
Figure: Principle of duty cycling used to reduce energy consumption in the region below Pe

## Slide 269
6.4 The Skylake-based processor lines
Notes: 269

## Slide 270: 6.4 The Skylake-based processor lines (1)
Key features of the Skylake lines -1 [202]
Dies: No. of cores GT level, e.g. 2+2 means: 2 cores +GT 2 graphics, etc.
6.4 The Skylake based processor lines

## Slide 271: 6.4 The Skylake-based processor lines (2)
Key features of the Skylake line -2 [190]

## Slide 272: 6.4 The Skylake-based processor lines (3)
Expected launch dates of the Skylakes Series [192]

## Slide 273: 6.4 The Skylake-based processor lines (4)
Mobiles (SoC designs)
4.5 W Core M-line (Y-line) (BGA1515)
Core m7-6Y7x, 2C+HD 515, HT, 9/2015
1. Introduction (2)
The Skylake (6th Gen) mobile and desktop lines - Overview
Core m5-6Y5x, 2C+HD 515, HT, 9/2015
Core m3-6Y3x, 2C+HD 515, HT, 9/2015
Core i7-66x0U/65x0U, 2C+HD 515, HT, 9/2015
Core i5-63x0U/62x0U, 2C+HD 515, HT, 9/2015
Core i3-6100U, 2C+HD 515, HT, 9/2015
15 W U-line (BGA1356)
Core i7-65x7U, 2C+HD 550, HT, 9/2015
Core i5-62x7U, 2C+HD 550, HT, 9/2015
Core i3-61x7U, 2C+HD 550, HT, 9/2015
28 W U-line (SoC, BGA1356)

## Slide 274: 6.4 The Skylake-based processor lines (5)
Desktops (2-chip designs, 100 Series chipset)
Core i7-6700T 4C+HD 530, HT, 9/2015
Core i5-6600T/6500T/6400T, 4C+HD 530, HT, 9/2015
Core i3-6300T/6100T, 2C+HD 530, HT, 9/2015
35 W S-lines (LGA 1151)
Core i7-6700K/6600K, 4C, HT, 8/2015
91 W S-lines, unlocked (LGA1151)
Microservers
45 W v5-lines (BGA)
Xeon E3-15x5M v5, 4C+HD 530, HT, 9/2015
Core i7-6920HQ/6820HQ/6700HQ, 4C+HD 530, HT, 9/2015
Core i5-6440HQ/6300HQ, 4C+HD 530, HT, 9/2015
Core i3-6100H, 2C+HD 530, HT, 9/2015
45 W HQ/H-lines (BGA1440)
Core i7-6700, 4C+HD 530, HT, 9/2015
Core i5-6600/6500/6400 4C+HD 530, HT, 9/2015
Core i3-6320/6300/6100, 2C+HD 530, HT, 9/2015
65 W S-lines (LGA 1151)

## Slide 275: 6.4 The Skylake-based processor lines (6)
Example 1: Main features of the models of the 4.5 W Skylake m-line [202]

## Slide 276: 6.4 The Skylake-based processor lines (7)
Example 2: Main features of the models of the 91 W unlocked Skylake S-line [202]
Note that the 91 W unlocked Skylake S-line does not include integrated graphics, as most users
of this high-end processor will attach discrete graphics cards.

## Slide 277: 6.4 The Skylake-based processor lines (8)
TDP (W) | No. of cores | Graphics | No. of graphics EUs | eDRAM | Base frequency (GHz)
4.5 | 2 | HD 515 | 18 | -- | 1.2
15 | 2 | HD 540 | 48 | 64 MB | 2.2
15 | 2 | HD 520 | 24 | -- | 2.6
28 | 2 | HD 550 | 48 | 64 MB | 3.3
35 | 4 | HD 530 | 24 | -- | 2.8
45 | 4 | HD 530 | 24 | -- | 2.9
65 | 4 | HD 530 | 24 | -- | 3.4
91 | 4 | -- | -- | -- | 4.2
The max. base frequency of Skylake models with different TDPs and configurations
(Based on data from [202])
Note that low TDP can be achieved first of all by reducing the core frequency and limiting
the computer resources (cores, GPU EUs) provided.

## Slide 278: 6.4 The Skylake-based processor lines (9)
Intel Core i7-6700K desktop processor platform [203]

## Slide 279
7. The Kaby Lake line
Notes: 279

## Slide 280: 7. The Kaby Lake line (1)
Preliminary information about the Kaby Lake line [179]
It is actually a Skylake refresh line manufacture on the 14 nm technology.
Announced on Intel’s Q2 2015 conference call.
Expected launch date: 2H 2016, it will be followed by the 10 nm Cannonlake in 2H 2017.
This means that the cadence of Intel’s technology transitions slowed down to about 2.5 years,
as Kranich, Intel’s CEO formulated:
The last two technology transitions have signaled that our cadence today is closer to
2.5 years than two."

## Slide 281: 7. The Kaby Lake line (2)
IMAGE
Variant | KBL-Y (BGA) | KBL-U (BGA) | KBL-H (BGA) | KBL-S (LGA) | KBL-S (LGA)
Cores Configurations | 2 | 2/2 | 4/4 | 2/4/4 | 4/4
Graphic Configurations | GT2 | GT2/GT3 | GT2/GT4 | GT2/GT2/GT4 | GT0/GT2
eDRAM | N/A | N/A / 64 MB | N/A / 256 MB | N/A / N/A/ 64 MB | N/A
SOC Design | Yes | Yes | No - External PCH | No - External PCH | No - External PCH
TDP | 4.5W | 15W / 28W | 35W / 45W / TBD | 35W / 65W / 91W | 25W / 45W / 80W
Expected main features of the Kaby Lake line [194]

## Slide 282: 7. The Kaby Lake line (3)
Expected system architecture of a U or Y-Series Kaby Lake processor [194]

## Slide 283
8. References
Notes: 283

## Slide 284: References (1)
[1]: Singhal R., “Next Generation Intel Microarchitecture (Nehalem) Family: Architecture Insight
and Power Management, IDF Taipeh, Oct. 2008, http://intel.wingateweb.com/taiwan08/
published/sessions/TPTS001/FA08%20IDFTaipei_TPTS001_100.pdf
[2]: Bryant D., “Intel Hitting on All Cylinders,” UBS Conf., Nov. 2007,
http://files.shareholder.com/downloads/INTC/0x0x191011/e2b3bcc5-0a37-4d06-
aa5a-0c46e8a1a76d/UBSConfNov2007Bryant.pdf
[3]: Fisher S., “Technical Overview of the 45 nm Next Generation Intel Core Microarchitecture
(Penryn),” IDF 2007, ITPS001, http://isdlibrary.intel-dispatch.com/isd/89/45nm.pdf
[4]: De Gelas J., “Intel Core versus AMD’s K8 architecture,” AnandTech, May 1 2006,
http://www.anandtech.com/cpuchipsets/intel/showdoc.aspx?i=2748&p=1
[5]: Carmean D., “Inside the Pentium 4 Processor Micro-architecture,” Aug. 2000,
http://people.virginia.edu/~zl4j/CS854/pda_s01_cd.pdf
[6]: Shimpi A. L. & Clark J., “AMD Opteron 248 vs. Intel Xeon 2.8: 2-way Web Servers
go Head to Head,” AnandTech, Dec. 17 2003,
http://www.anandtech.com/showdoc.aspx?i=1935&p=1
[7]: Völkel F., “Duel of the Titans: Opteron vs. Xeon : Hammer Time: AMD On The Attack,”
Tom’s hardware, Apr. 22 2003,
http://www.tomshardware.com/reviews/duel-titans,620.html
[8]: De Gelas J., “Intel Woodcrest, AMD's Opteron and Sun's UltraSparc T1:
Server CPU Shoot-out,” AnandTech, June 17 2006,
http://www.anandtech.com/IT/showdoc.aspx?i=2772&p=1

## Slide 285: References (2)
[10]: Wechsler O., “Inside Intel Core Microarchitecture,” White Paper, Intel, 2006
[11]: Lee V., “Inside the Intel Core Microarchitecture,” IDF, May 2006, Shenzhen,
http://www.prcidf.com.cn/sz/systems_conf/track_sz/SMC/Intel%20Core%20uArch.pdf
[12]: Doweck J., “Inside Intel Core Microarchitecture,” Hot Chips 18, 2006,
http://www.hotchips.org/archives/hc18/
[13]: Gruen H., “Intel’s new Core Microarchitecture,” Develop Brighton, AMD Technical
Day, July 2006,
http://ati.amd.com/developer/brighton/03%20Intel%20MicroArchitecture.pdf
[14]: Doweck J., “Intel Smart Memory access: Minimizing Latency on Intel Core
Microarchitecture, ” Technology @ intel Magazine, Sept. 2006, pp. 1-7,
ftp://download.intel.com/corporate/pressroom/emea/deu/fotos/06-10-Strategie_Tag/
Intel/Intel_Core2_Prozessoren/Texte/ENG-Smart_Memory_Access_Technology@
Intel_Magazine_Article.pdf
[15]: Sima D., Fountain T., Kacsuk P., Advanced Computer Architectures, Addison Wesley,
Harlow etc., 1997
[16]: Jafarjead B., “Intel Core Duo Processor,” Intel, 2006,
http://masih0111.persiangig.com/document/peresentation/behrooz%20jafarnejad.ppt
[17]: Pawlowski S. & Wechsler O., “Intel Core Microarchitecture,” IDF Spring, 2006,
http://www.intel.com/pressroom/kits/core2duo/pdf/ICM_tech_overview.pdf
[9]: Hinton G. & al., “The Microarchitecture of the Pentium 4 Processor,” Intel Technology
Journal, Q1 2001, pp. 1-13

## Slide 286: References (3)
[21]: Kim N. S. et al., „Leakage Current: Moore’s Law Meets Static Power”, Computer,
Dec. 2003, pp. 68-75.
[22]: Ng P. K., “High End Desktop Platform Design Overview for the Next Generation
Intel Microarchitecture (Nehalem) Processor,” IDF Taipei, TDPS001, 2008,
http://intel.wingateweb.com/taiwan08/published/sessions/TDPS001/
FA08%20IDF-Taipei_TDPS001_100.pdf
[23]: Bohr M., Mistry K., Smith S., “Intel Demonstrates High-k + Metal Gate Transistor
Breakthrough in 45 nm Microprocessors,”, Intel, Jan. 2007,
http://download.intel.com/pressroom/kits/45nm/Press45nm107_FINAL.pdf
[24]: Scott D. S., “Toward Petascale and Beyond,” APAC Conference, Oct. 2007,
http://www.apac.edu.au/apac07/pages/program/presentations/
Tuesday%20Harbour%20A%20B/David_Scott.pdf
[25]: Smith S. L., “45 nm Product Press Briefing,” IDF Fall, 2007,
http://download.intel.com/pressroom/kits/events/idffall_2007/BriefingSmith45nm.pdf
[26]: Fisher S., “Technical Overview of the 45nm Next Generation Intel Core Microarchitecture
(Penryn),” IPTS001, Fall IDF 2007, http://isdlibrary.intel-dispatch.com/isd/89/45nm.pdf
[19]: SIMD Instruction Sets, http://softpixel.com/~cwright/programming/simd/index.php
[20]: Wikipedia: Platform Environment Control Interface,
http://en.wikipedia.org/wiki/Platform_Environment_Control_Interface
[18]: Goto H., Larrrabee architecture can be integrated into CPU”, PC Watch, Oct. 6 2008,
http://pc.watch.impress.co.jp/docs/2008/1006/kaigai470.htm

## Slide 287: References (4)
[31]: Gelsinger P. P., “Intel Architecture, Press Briefing, March 2008,
http://www.slideshare.net/angsikod/gelsinger-briefing-on-intel-architecture
[32]: Gelsinger P., “Invent the new reality,” IDF Fall 2008, San Francisco
http://download.intel.com/pressroom/kits/events/idffall_2008/PatGelsinger_day1.pdf
[33]: Brayton J.,”Nehalem: Talk of the Tock, Intel Next Generation Microprocessor,” IDF,
April 2008, Shanghai,
http://inteldeveloperforum.com.edgesuite.net/shanghai_2008/ti/TCH001/f.htm
[34]: Intel Timna Microprocessor Family, CPU World, http://www.cpu-world.com/CPUs/Timna/
[35]: Smith T., “Timna - Intel's first system-on-a-chip, Before 'Tolapai', before 'Banias'.
Register Hardware, Febr. 6 2007,
http://www.reghardware.co.uk/2007/02/06/forgotten_tech_intel_timna/
[28]: Wikipedia: Foxton Technology, http://en.wikipedia.org/wiki/Foxton_Technology
[29]: Coke J. & al., “Improvements in the Intel Core Penryn Processor Family Architecture
and Microarchitecture,” Intel Technology Journal, Vol. 12, No. 3, 2008, pp. 179-192
[30]: Fisher S., “Technical Overview of the 45nm Next Generation Intel Core Microarchitecture
(Penryn),” BMA S004, IDF 2007,
http://my.ocworkbench.com/bbs/attachment.php?attachmentid=318&d=1176911500
[27]: George V., 45nm Next Generation Intel Core Microarchitecture (Penryn),” Hot Chips 19,
2007, http://www.hotchips.org/archives/hc19/3_Tues/HC19.08/HC19.08.01.pdf

## Slide 288: References (5)
[38]: Strong B., “A Look Inside Intel: The Core (Nehalem) Microarchitecture,”
http://www.cs.utexas.edu/users/cart/arch/beeman.ppt
[39]: Valles A. C., Ansari Z., Mehrotra P.: “Tuning Your Software for the Next Generation
Intel Microarchitecture (Nehalem) Family,” IDF 2008, NGMS002,
http://www.benchmark.rs/tests/editorial/Nehalem_munich/presentations/
Software-Tuning_for_Nehalem.pdf
[40]: The low cost Tymna CPU, Tom’s hardware, Febr. 25 2000,
http://www.tomshardware.com/reviews/idf-2000,166-3.html
[41]: Intel® Virtualization Technology, Special issue, Vol. 10 No. 03 Aug. 2006, http://www.intel.com/technology/itj/2006/v10i3/
[37]: Singhal R. Intel’s i7, Podtech, http://www.podtech.net/home/5436/intels-core-i7
[36]: Images, Xtreview,
http://xtreview.com/images/K10%20processor%2045nm%20architec%203.jpg
[42]: Intel Core 2 Duo Processor E8000 and E7000 Series Datasheet, Intel, Jan. 2009
[43]: Wikipedia: List of Intel Core 2 microprocessors
http://en.wikipedia.org/wiki/List_of_Intel_Core_2_microprocessors
[44]: Wikipedia: Nehalem (microarchitecture)
http://en.wikipedia.org/wiki/Nehalem_(microarchitecture)
[45]: Glaskowsky P.: Investigating Intel's Lynnfield mysteries, cnet News, Sept. 21 2009,
http://news.cnet.com/8301-13512_3-10357328-23.html

## Slide 289: References (6)
[48]: Intel CoreTM i7-800 and i5-700 Desktop Processor Series Datasheet – Volume 1,
July 2010, http://download.intel.com/design/processor/datashts/322164.pdf
[50]: Intel CoreTM i7-900 Mobile Processor Extreme Edition Series, Intel Core i7-800 and
i7-700 Mobile Processor Series, Datasheet – Volume One, Sept. 2009
http://download.intel.com/design/processor/datashts/320765.pdf
[51]: Intel Turbo Boost Technology in Intel CoreTM Microarchitecture (Nehalem) Based
Processors, White Paper, Nov. 2008 http://download.intel.com/design/processor/applnots/320354.pdf
[47]: Intel Xeon Processor C5500/C3500 Series, Datasheet – Volume 1, Febr. 2010,
http://download.intel.com/embedded/processor/datasheet/323103.pdf
[46]: Shimpi A. L.: Intel's Core i7 870 & i5 750, Lynnfield: Harder, Better, Faster Stronger,
AnandTech, Sept. 8 2009, http://www.anandtech.com/show/2832
[52]: Power Management in Intel Architecture Servers, White Paper, April 2009
http://download.intel.com/support/motherboards/server/sb/power_management_
of_intel_architecture_servers.pdf
[53]: Glaskowsky P.: Explaining Intel’s Turbo Boost technology, cnet News, Sept. 28 2009,
http://news.cnet.com/8301-13512_3-10362882-23.html
[49]: Glaskowsky P.: Intel's Lynnfield mysteries solved, cnet News, Sept. 28 2009,
http://news.cnet.com/8301-13512_3-10362512-23.html
[54]: Intel Xeon Processor 7500 Series, Datasheet – Volume 2, March 2010
http://www.intel.com/Assets/PDF/datasheet/323341.pdf

## Slide 290: References (7)
[58]: Hill D., Chowdhury M.: Westmere Xeon-56xx „Tick” CPU, Hot Chips 2010
http://www.hotchips.org/uploads/archive22/HC22.24.620-Hill-Intel-WSM-EP-print.pdf
[59]: Intel CoreTM i7-600, i5-500, i5-400 and i3-300 Mobile Processor Series, Datasheet -
Vol.1, Jan. 2010, http://download.intel.com/design/processor/datashts/322812.pdf
[56]: Kottapalli S., Baxter J.: Nehalem-EX CPU Architecture, Hot Chips 2009, Sept. 10 2009
http://www.hotchips.org/archives/hc21/2_mon/HC21.24.100.ServerSystemsI-Epub/
HC21.24.122-Kottapalli-Intel-NHM-EX.pdf
[55]: Pawlowski S.: Intelligent and Expandable High- End Intel Server Platform, Codenamed
Nehalem-EX, IDF 2009
[60]: Nagaraj D., Kottapalli S.: Westmere-EX: A 20 thread server CPU, Hot Chips 2010
http://www.hotchips.org/uploads/archive22/HC22.24.610-Nagara-Intel-6-Westmere-EX.pdf
[57]: Kurd N. A. & all: A Family of 32 nm IA Processors, IEEE Journal of Solide-State Circuits,
Vol. 46, Issue 1., Jan. 2011, pp. 119-130
[61]: Kahn O., Piazza T., Valentine B.: Technology Insight: Intel Next Generation
Microarchitecture Codename Sandy Bridge, IDF 2010
extreme.pcgameshardware.de/.../281270d1288260884-bonusmaterial-pc- games-
hardware-12-2010-sf10_spcs001_100.pdf
[62]: Wikipedia: Sandy Bridge, http://en.wikipedia.org/wiki/Sandy_Bridge
[63]: http://ark.intel.com
[64]: Kahn O., Valentine B.: Intel Next Generation Microarchitecture Codename Sandy Bridge:
New Processor Innovations, IDF 2010

## Slide 291: References (8)
[65]: Shimpi A. L.: Intel Pentium 4 1.4GHz & 1.5GHz, AnandTech, Nov. 20 2000
http://www.anandtech.com/show/661/5
[66]: Yuffe M., Knoll E., Mehalel M., Shor J., Kurts T.: A fully integrated multi-CPU, GPU and
memory controller 32nm processor, ISSCC, Febr. 20-24 2011, pp. 264-266
[67]: Intel Xeon Processor 7500/6500 Series, Public Gold Presentation, Data Center Group,
March 30. 2010, http://cache-www.intel.com/cd/00/00/44/64/446456_446456.pdf
[68]: Tang H., Cheng H.: Intel Xeon Processor E3 Family Based Servers: A Smart Investment
for Managing Your Small Business, IDF 2011
[69]: Thomadakis M. E. PhD: The Architecture of the Nehalem Processor and Nehalem-EP SMP
Platforms, Texas A&M University, March 17 2011
http://alphamike.tamu.edu/web_home/papers/perf_nehalem.pdf
[70]: Intel Xeon Processor E7-8800/4800/2800 Product Families, Datasheet Vol. 1 of 2,
April 2011, http://www.intel.com/Assets/PDF/datasheet/325119.pdf
[71]: Mitchell D., Intel Nehalem-EX review, PCPro,
http://www.pcpro.co.uk/reviews/processors/357709/intel-nehalem-ex
[72]: Rusu & al.: A 45 nm 8-Core Enterprise Xeon Processor, IEEE journal of Solid State Circuits,
Vol. 45, No. 1, Jan. 2010, pp. 7-14
[73]: Wechsler O., Multicore Archtecture Challenges and Opportunities, Intel’s Annual Symposium
on VLSI CAD and Validation, Keynote presentation, July 2007
http://www3.ee.technion.ac.il/sites/Workshop/upload/Events/ACRC%20-%20Intel/
Ofri-Wechsler%20Keynotes%20Speech.pdf

## Slide 292
References (9)
[74]: Razin A., Core, Nehalem, Gesher. Intel: New Architecture Every Two Years,
Xbit Laboratories, April 28 2006,
http://www.xbitlabs.com/news/cpu/display/20060428162855.html
[75]: Har_Even B., Justin Rattner Keynote? Trusted Reviews, April 17 2007,
http://www.trustedreviews.com/news/IDF-Spring-2007-Day-One-Opening-Keynote
[76]: Weatherstone R., Intel Core i7-3960X Extreme Edition Processor (Sandy Bridge-E)
Review, Nov. 14 2011, Vortez, http://www.vortez.net/articles_pages/intel_core_i7_
3960x_extreme_edition_processor_sandy_bridge_e,2.html
[77]: Shimpi A. L., Intel Core i7 3960X (Sandy Bridge E) Review: Keeping the High End Alive,
Nov. 14 2011, AnandTech, http://www.anandtech.com/show/5091/intel-core-i7-3960x-
sandy-bridge-e-review-keeping-the-high-end-alive/4
[78]: Intel® X79 Express Chipset, http://www.intel.com/content/www/us/en/chipsets/
performance-chipsets/x79-express-chipset.html
[79]: Intel® Desktop Board DX79SI Extreme Series, 2011, http://www.intel.com/content/
dam/doc/product-brief/desktop-board-dx79si-extreme-brief.pdf
[81]: Olivera, A régóta várt Intel Ivy Bridge tesztje, Prohardware, April 13 2012,
http://prohardver.hu/teszt/intel_ivy_bridge_teszt/az_ivy_bridge.html
[80]: Chappell R., Toll B., Singhal R.: Intel Next Generation Microarchitecture Codename Haswell:
New Processor Innovations, IDF 2012

## Slide 293
[82]: Bohr M., Mistry K.: Intel’s Revolutionary 22 nm transistor technology, May 2011,
http://download.intel.com/newsroom/kits/22nm/pdfs/22nm-Details_Presentation.pdf
[83]: George V., Piazza T., Jiang H.: Technology Insight: Intel Next Generation Microarchitecture
Codename Ivy Bridge, IDF 2011
[84]: 3rd Generation Intel Core Processor Family Quad Core Launch Product Information,
April 23 2012, http://download.intel.com/newsroom/kits/core/3rdgen/pdfs/3rd_Generation
_Intel_Core_Product_Information.pdf
[85]: Ivy Bridge and Haswell die configurations (estimates included), Anandtech, March 21 2012,
http://forums.anandtech.com/showthread.php?t=2234017
[86]: Piazza T., Jiang H., Hammerlund P., Singhal R.: Technology Insight: Intel Next Generation
Microarchitecture Codename Haswell, IDF 2012 SPCS001
[87]: Haynes D.: 2012 Socket Guide, Aug. 4 2012,
http://www.ocmodshop.com/cpu-socket-guide-2012/lga2011/
[88]: O’Shea P., Thermal management solutions include support for Intel platform environmental
control interface, EE Times, Oct. 17 2006,
http://www.eetimes.com/document.asp?doc_id=1301982
[90]: Shimpi A. L., The Intel Core i3 530 Review - Great for Overclockers & Gamers,
AnandTech, Jan. 22 2010, http://www.anandtech.com/show/2921
[89]: Altavilla D., Intel Arrandale Core i5 and Core i3 Mobile Unveiled, Hot Hardware, Jan. 4 2010,
http://hothardware.com/Reviews/Intel-Arrandale-Core-i5-and-Core-i3-Mobile-Unveiled/
References (10)

## Slide 294
[91]: Chiappetta M., Intel Clarkdale Core i5 Desktop Processor Debuts, Hot Hardware, Jan. 3 2010,
http://hothardware.com/Articles/Intel-Clarkdale-Core-i5-Desktop-Processor-Debuts/
[92]: Thomas S. L., Desktop Platform Design Overview for Intel Microarchitecture (Nehalem)
Based Platform, Presentation ARCS001, IDF 2009
[93]: Kirsch N., Intel Core i7-980X Six-Core Processor Extreme Edition Review, Legit Reviews,
March 11 2010, http://www.legitreviews.com/intel-core-i7-980x-six-core-processor-
extreme-edition-review_1245
[94]: Kanter D., Westmere Arrives, Real World Tech, March 17 2010,
http://www.realworldtech.com/westmere/2/
[95]: Hruska J., Intel Unveils 10-Core Xeons, Mission-Critical Servers, Hot Hardware, Apr. 5 2011,
http://hothardware.com/Reviews/Intel-Unveils-10Core-Xeons-MissionCritical-Servers/
[96]: Intel Sandy Bridge Review, Bit-tech, Jan. 3 2011,
http://www.bit-tech.net/hardware/cpus/2011/01/03/intel-sandy-bridge-review/1
[97]: Toll B., Locktyukhin M., Girkar M., Intel Advanced Vector Extensions 2 and Bit Manipulation
New Instructions, IDF 2012
[99]: Piazza T., Dr. Jiang H., Microarchitecture Codename Sandy Bridge: Processor
Graphics, Presentation ARCS002, IDF San Francisco, Sept. 2010
[98]: Torres G., Inside the Intel Sandy Bridge Microarchitecture, Hardware Secrets, Dec. 30 2010,
http://www.hardwaresecrets.com/article/Inside-the-Intel-Sandy-Bridge-Microarchitecture/1161/2
References (11)

## Slide 295
[100]: Wikipedia: Intel GMA, 2011, http://en.wikipedia.org/wiki/Intel_GMA
[101]: Shimpi A. L., The Sandy Bridge Review: Intel Core i7-2600K, i5-2500K and Core i3-2100
Tested, AnandTech, Jan. 3 2011, http://www.anandtech.com/show/4083/the-sandy-
bridge-review-intel-core-i7-600k-i5-2500k-core-i3-2100-tested/11
[102]: Intel® Q67 Express Chipset, http://www.intel.com/content/www/us/en/chipsets/
mainstream-chipsets/q67-express-chipset.html
[103]: Rodolf K., Small and Medium Business Server Solutions from Intel, Sept. 20 2012
[104]: Intel Core i7 Processor Family for the LGA-2011 Socket, Datasheet, Vol.1, Nov. 2012,
http://www.intel.com/content/www/us/en/processors/core/core-i7-lga-2011-datasheet-
vol-1.html
[105]: Crijns K., nVidia GeForce GTX 680 Quad-SLI review, Hardware.info, March 23 2012,
http://nl.hardware.info/reviews/2641/nvidia-geforce-gtx-680-quad-sli-review-english-version
[106]: Wikipedia: List of Intel Xeon microprocessors,
http://en.wikipedia.org/wiki/List_of_Intel_Xeon_microprocessors#Sandy_Bridge-based_Xeons
[108]: Intel Xeon E5-2690 001, CPU, Tom’s Hardware, http://www.tomshardware.com/gallery/
Intel-Xeon-E5-2690-001,0101-320460-0-2-3-1-jpg-.html
[107]: Morgan T.P., Intel plugs both your sockets with 'Jaketown' Xeon E5-2600s, The Register,
March 6 2012, http://www.theregister.co.uk/2012/03/06/intel_xeon_2600_server_
chip_launch/
References (12)

## Slide 296
[109]: System Architecture and Configuration, Oct. 2012,
http://www.qdpma.com/systemarchitecture/SystemArchitecture_2012Q4.html
[110]: Intel Xeon Processor E5-1600/E5-2600/E5-4600 Product Families, Datasheet, Vol.1,
May 2012, http://www.intel.la/content/www/xl/es/processors/xeon/xeon-e5-1600-2600-
vol-1-datasheet.html
[111]: Bolaria J., Romley Revamps Server Platforms, The Linley Group, April 2 2012,
http://www.linleygroup.com/mpr/article.php?id=10879
[112]: Angelini C., Intel Xeon E5-2600: Doing Damage With Two Eight-Core CPUs, Tom’s Hardware,
March 6 2012, http://www.tomshardware.com/reviews/xeon-e5-2687w-benchmark-
review,3149-10.html
[113]: Ulvr P., Fait F., Built to Scale: Introducing the Intel Xeon Processor E5 Family, 2012,
http://www-05.ibm.com/cz/events/truck2012/bp/pdf/system_x_cast/Intel_Xeon_E5_
obchodni.pdf
[114]: Panagiotidis N.G., Intel Xeon: the Enabling Technology to the Performing, Flexible & Energy
efficient Cloud Infrastructure, April 23 2013,
http://www.cisco.com/web/GR/connect2013/pdfs/007_intel_nikos_panagiotidis.pdf
[116]: Vilches J., Intel Ivy Bridge: everything you need to know, TechSpot, March 8 2012,
http://www.techspot.com/guides/502-intel-ivy-bridge/page3.html
[115]: Wikipedia: Ivy Bridge (microarchitecture),
http://en.wikipedia.org/wiki/Ivy_Bridge_%28microarchitecture%29
References (13)

## Slide 297
[117]: Shimpi A.L., Intel Iris Pro 5200 Graphics Review: Core i7-4950HQ Tested, AnandTech,
June 1 2013, http://www.anandtech.com/show/6993/intel-iris-pro-5200-graphics-
review-core-i74950hq-tested
[118]: Product Brief Intel Xeon Processor E3-1200 v2 Product Family, 2012,
http://software.intel.com/sites/products/vcsource/files/xeon-e3-1200v2-brief__2_.pdf
[119]: Leberecht M., Expanding Intel Architecture Flexibility in the Data Center, March 20 2013,
http://www.worldhostingdays.com/downloads/2013/hStag2a1.pdf
[120]: Wikipedia: Haswell (microarchitecture),
http://en.wikipedia.org/wiki/Haswell_%28microarchitecture%29
[121]: Von Holzbauer F., Kugler A., Neue Intel-Architektur mit Grafik-Fokus, Chip Online,
June 1 2013, http://www.chip.de/artikel/Intel-Haswell-Neue-CPUs-fuer-Notebooks-und-
PCs_62209040.html
[122]: Valentine B., Intel Next Generation Microarchitecture Codename Haswell: New Processor
Innovations, 2012, http://ftp.software-sources.co.il/Processor_Architecture_Update-
Bob_Valentine.pdf
[124]: Scansen D., Intel Launches Next Generation of Microprocessors, Engineering, June 10 2013,
http://www.engineering.com/ElectronicsDesign/ElectronicsDesignArticles/ArticleID/
5838/Intel-Launches-Next-Generation-of-Microprocessors.aspx
[123]: Brown M., Intel lifts the veil on Haswell graphics, PC World, May 2 2013,
http://www.pcworld.com/article/2037063/intel-lifts-the-veil-on-haswell-graphics.html
References (14)

## Slide 298
[125]: Walton J., Hit the Road, Jack: Intel’s Mobile Quad-Core Haswell SKUs, AnandTech,
June 1 2013, http://www.anandtech.com/show/7002/hit-the-road-jack-intels-mobile-
quadcore-haswell-skus
[126]: Walton J., Intel’s Haswell: Quad-Core Desktop Processor SKUs, AnandTech, June 1 2013,
http://www.anandtech.com/show/7001/intels-haswell-quadcore-desktop-processor-skus
[127]: Kirsch N., Intel Core i7-4770K Haswell Processor Performance Review Posted, Legit Reviews,
March 18 2013, http://www.legitreviews.com/intel-core-i7-4770k-haswell-processor-
performance-review-posted_15286
[128]: Kennedy P., Intel Xeon E3-1200 V3 Series Compute Value Comparison, STH, June 13 2013,
http://www.servethehome.com/intel-xeon-e3-1200-v3-series-compute-comparison/
[129]: Kennedy P., Leaked Intel Xeon E3-1200 V3 Series and Comparison to V1 and V2, STH,
April 3 2013, http://www.servethehome.com/leaked-intel-xeon-e3-1200-v3-series-
comparison-v1-v2/
[130]: Intel® Xeon® Processor E3-1200 v3 Product Family with Intel® HD Graphics P4600 and
Intel® C226 Chipset: Block Diagram, http://www.intel.com/content/www/us/en/
intelligent-systems/denlow/xeon-e3-1200-v3-c266-chipset-ibd.html
[132]: Intel Core i7 High End Desktop Processor Family for Socket LGA-2011, Aug. 2013,
[131]: Chiappetta M., Intel Core i7-4960X Ivy Bridge-E CPU Review, Hot Hardware,
Sept. 3 2013, http://hothardware.com/Reviews/Intel-Core-i74690X-Extreme-Edition-
Ivy-Bridge-E-CPU-Review/?page=2
References (15)

## Slide 299
[133]: Pop S., Intel Releases Core i7 Extreme Central Processing Units, Softpedia, Sept. 9 2013,
http://news.softpedia.com/news/Intel-Releases-Core-i7-Extreme-Central-Processing-
Units-381369.shtml
[134]: Shimpi A.L., Intel Core i7 4960X (Ivy Bridge E) Review, AnandTech, Sept. 3 2013,
http://www.anandtech.com/show/7255/intel-core-i7-4960x-ivy-bridge-e-review
[135]: Hruska J., Core i7-4960X Ivy Bridge-E review: Intel’s Great Limp Forward, ExtremeTech,
Sept. 3 2013, http://www.extremetech.com/gaming/165498-core-i7-4960x-ivy-bridge-e-
review-intels-great-limp-forward
[136]: Novakovic N., Intel Xeon 2013 update – A bit later, but a bit better too, VR-Zone,
April 9 2013, http://vr-zone.com/articles/intel-xeon-2013-update--a-bit-later-but-a-bit-
better-too/19581.html?utm_source=feedburner&utm_medium=feed&utm_campaign=
Feed%3A+TheTomorrowTimes+%28The+Tomorrow+Times%29
[137]: De Gelas J., Intel's Xeon E5-2600 V2: 12-core Ivy Bridge EP for Servers, AnandTech,
Sept. 17 2013, http://www.anandtech.com/show/7285/intel-xeon-e5-2600-v2-12-core-
ivy-bridge-ep
[139]: Eshelman E., Intel Xeon E5-2600v2 “Ivy Bridge” Processor Review, Microway,
Sept. 10 2013, http://www.microway.com/hpc-tech-tips/intel-xeon-e5-2600v2-ivy-
bridge-processor-review/
[138]: Morgan T.P., Intel carves up Xeon E5-2600 v2 chips for two-socket boxes, The Register,
Sept. 10 2013, http://www.theregister.co.uk/2013/09/10/intel_ivy_bridge_xeon_e5_
2600_v2_launch/
References (16)

## Slide 300
[140]: Shvets A., Intel Xeon E5-1600 v2 and E5-2600 v2 CPUs launched, CPU World,
Sept. 14 2013, http://www.cpu-world.com/news_2013/2013091401_Intel_Xeon_
E5-1600_v2_and_E5-2600_v2_CPUs_launched.html
[141]: Mujtaba H., Intel Ivy Bridge-EX Confirmed To Feature 15 Cores – Arrives in 2H 2013,
WCCF Tech, 2013, http://wccftech.com/intel-ivy-bridge-ex-feature-15-cores/
[142]: Shvets G., Some details of upcoming Intel Xeon E5 v2 and E7 v2 CPUs, CPU World,
April 2 2013, http://www.cpu-world.com/news_2013/2013040201_Some_details_of_
upcoming_Intel_Xeon_E5_v2_and_E7_v2_CPUs.html
[143]: Mouthaan M., Intel Haswell-E slides published; DDR4 and octa-cores, Hardware Info,
June 16 2013, http://us.hardware.info/news/35581/intel-haswell-e-slides-published-
ddr4-and-octa-cores
[144]: Introducing the 4th Generation Intel Core Processor (code-named Haswell), 2013,
http://software.intel.com/sites/default/files/introduction-to-intel-4th-generation-core-
processor.pdf
References (17)
[145]: Unparalleled Performance and Responsiveness, Product Brief, Intel Z87 Chipset, 2013,
http://www.intel.com/content/dam/www/public/us/en/documents/product-briefs/
z87-chipset-brief.pdf
[146]: Haas, J. & Vogt P., Fully buffered DIMM Technology Moves Enterprise Platforms to the
Next Level,” Technology Intel Magazine, March 2005, pp. 1-7
Intel Xeon processor E3-1200 v3 Product Family and the Emergence of Graphics in the
Cloud, June 3 2013,
http://www.yumpu.com/en/document/view/18758369/cover-slide-title-intel-newsroom
[147]:

## Slide 301
[148]: Gasior G., Leaked slides expose Haswell's integrated voltage regulator, May 13, 2013,
http://techreport.com/news/24802/leaked-slides-expose-haswell-integrated-voltage-
regulator
References (18)
[149]: Hammerlund P. & al., Haswell: The Fourth Generation Intel Core Processor, IEEE MICRO
March/April 2014, pp. 6-20
[150]: Burton E.A. & al., FIVR – Fully Integrated Voltage Regulators on 4th Generation Intel
Core™ SoCs, Proc. Twenty-Ninth Annual IEEE Applied Power Electronics Conference and
Exposition (APEC), 2014, pp. 432 - 439
[151]: Application Note: Atmel AT04204: Design a Buck Converter with XMEGA E, Atmel Corp.
2013, http://www.atmel.com/Images/Atmel-42183-Design-a-Buck-Converter-with-
XMEGA-E_AP-Note_AT04204.pdf
[152]: Buck converter, http://en.wikipedia.org/wiki/Buck_converter
[153]: Borkar R., A Multy Year Journey, Aug. 11 2014, Intel,
http://download.intel.com/newsroom/kits/14nm/pdfs/Intel_14nm_New_uArch.pdf
[154]: Bohr M., 14 nm Technology Announcement, Aug. 11 2014, Intel,
http://download.intel.com/newsroom/kits/14nm/pdfs/Intel_14nm_New_uArch.pdf
[155]: Jourdan S., Broadwell Microarchitecture Disclosure, Aug. 11 2014, Intel,
http://download.intel.com/newsroom/kits/14nm/pdfs/Intel_14nm_New_uArch.pdf
[156]: Chennupaty S., Jiang H., Sreenivas A., Technology insight: Intel’s Next Generation 14 nm
Microarchitecture for Client and Server, IDF 2014 SPCS002, San Francisco, 2014,
https://intel.activeevents.com/sf14/connect/sessionDetail.ww?SESSION_ID=1204

## Slide 302
[158]: Smith S.L., Intel Strategy & Technology Update, Barclays Capital Global Technology Conf.,
Dec. 2011, http://files.shareholder.com/downloads/INTC/1576180143x0x526852/c9868a
3a-494e-4506-bcc6-a631aca1fd75/Steve%20Smith%20Barclays%20Dec%202011.pdf
[159]: Kanter D., Intel’s merom Unveiled, Real World Technologies, March 9, 2006,
http://www.realworldtech.com/merom/6/
[160]: Kanter D., Inside Barcelona: AMD's Next Generation, Real World Technologies, May 9, 2007,
http://www.hypertransport.org/docs/news/rwtech_inside_barcelona_05-16-07.pdf
[161]: - Intel 64 and IA-32 Architectures Software Developer’s Manual Combined Volumes:
1, 2A, 2B, 2C, 3A, 3B and 3, Intel, Order Number: 325462-052US, September 2014,
http://www.intel.com/content/dam/www/public/us/en/documents/manuals/64-ia-32-
architectures-software-developer-manual-325462.pdf
[162]: - SSE, The Free Dictionary, http://encyclopedia2.thefreedictionary.com/Supplemental+SSE3
[163]: Doweck J., Inside Intel Core Microarchitecture, Hot Chips 18, 2006,
http://www.hotchips.org/wp-content/uploads/hc_archives/hc18/3_Tues/HC18.S9/
HC18.S9T4.pdf
[164]: Goto H., ARM Cortex – A Family Architecture, 2010,
http://pc.watch.impress.co.jp/video/pcw/docs/423/409/p1.pdf
References (19)
[157]: Junkins S., The Compute Architecture of Intel Processor Graphics Gen8, IDF 2014,
https://software.intel.com/sites/default/files/managed/71/a2/Compute%20Architecture%
20of%20Intel%20Processor%20Graphics%20Gen8.pdf

## Slide 303
[167]: Shimpi A. L., Intel’s Core i7 870 C i5 750 Lynnfield: Harder, Better, Faster, Stronger,
AnandTech, Sept. 8, 2009, http://www.anandtech.com/show/2832/2
References (20)
[168]: Lomont C., Introduction to Intel® Advanced Vector Extensions, Intel, 23 May 2011,
https://software.intel.com/sites/default/files/m/d/4/1/d/8/Intro_to_Intel_AVX.pdf
[169]: Intel QuickPath Interconnect Electrical Architecture Overview, Intel, 2010,
http://jamesstovalldesign.files.wordpress.com/2012/08/pages-from-intel_qpied_final_
03-18-10.pdf
[170]: Davis L., PCI Express Bus,
http://www.interfacebus.com/PCI-Express-Bus-PCIe-Description.html
[171]: Wasson S., Intel's Xeon E5-2687W v3 processor reviewed, TechReport, Sept. 8 2014,
http://techreport.com/review/27018/intel-xeon-e5-2687w-v3-processor-reviewed
[172]: Klemm M., The Intel Platform for High Performance Computing, Intel, Oct. 07 2014
https://sharepoint.campus.rwth-aachen.de/units/rz/HPC/public/Shared%20Documents/
2014-10-07_aiXcelerate-01_Intel_Architecture-Haswell+Xeon_Phi.pdf
[173]: Moen M., Ragland D., Guerrero JJ., Overclocking Unlocked Intel Core Processors for
High Performance Gaming and Content Creation, IDF 2013, San Francisco, Sept. 1 2013,
AIOS001
[165]: Borges L., Intel Technologies for High Performance Computing, Intel Software Solution
Conference 2014 Brazil, May 2014,
http://www.slideshare.net/IntelSoftwareBR/hpc-update-istep2014
[166]: Intel Core 2 Duo Processor, http://www.intel.com/pressroom/kits/core2duo/

## Slide 304
[174]: Wikipedia, Intel HD and Iris Graphics,
https://en.wikipedia.org/wiki/Intel_HD_and_Iris_Graphics
[175]: Intel Xeon Processor E3-1200 Product Family, Product Brief, 2011
[176]: Cutress I., The Intel Haswell Refresh Review: Core i7-4790, i5-4690 and i3-4360 Tested,
AnandTech, May 11 2014, http://www.anandtech.com/show/7963/the-intel-haswell-
refresh-review-core-i7-4790-i5-4690-and-i3-4360-tested/2
[177]: Altavilla D., Intel 5th Gen Core Series Mobile Processors A Huge Deal For Thin And Light
Notebooks, Forbes, Jan. 8 2015, http://www.forbes.com/sites/davealtavilla/2015/01/08/
intel-5th-gen-core-series-mobile-processors-a-huge-deal-for-thin-and-light-notebooks/
[178]: Campbell M., Intel to Bring back FIVR after Skylake and Kaby Lake CPUs, Overclock 3D,
July 13 2015, http://www.overclock3d.net/articles/cpu_mainboard/intel_to_bring_
back_fivr_after_skylake_and_kaby_lake_cpus/1
[179]: Howse B., Smith R., Tick Tock On The Rocks: Intel Delays 10nm, Adds 3rd Gen 14nm Core
Product "Kaby Lake„, AnandTech, July 16 2015,
http://www.anandtech.com/show/9447/intel-10nm-and-kaby-lake
[181]: Cutress I., The Intel Broadwell Desktop Review: Core i7-5775C and Core i5-5675C Tested
(Part 1), AnandTech, June 2 2015,
http://www.anandtech.com/show/9320/intel-broadwell-review-i7-5775c-i5-5675c
[180]: Intel's (INTC) CEO Brian Krzanich on Q2 2015 Results - Earnings Call Transcript, Seeking
Alpha, July 15 2015, http://seekingalpha.com/article/3329035-intels-intc-ceo-brian-
krzanich-on-q2-2015-results-earnings-call-transcript?page=2
References (21)

## Slide 305
[182]: Johnson H., Voltage-Regulator Droop, Signal Consulting, Sept. 14 2006,
http://www.sigcon.com/Pubs/edn/VoltageRegulatorDroop.htm
[183]: Chennupaty S., Jiang H., Intel’s 14 nm Microarchitecture (Broadwell), IDF15
[184]: Hux A, 5th Generation Intel Core Processor Graphics: Gen8 Compute Architecture,
IDF15, GVCS001
[185]: Woligroski D., Intel's Broadwell Core M Processor: New Details, SKUs and Specifics,
Tom’s Hardware, Sept. 5 2014,
http://www.tomshardware.com/news/intel-broadwell-core-m,27596.html
[186]: Mujtaba H., Intel’s 14nm Core M Series “Broadwell-Y” Processors With 4.5W TDP Detailed –
Powers Fanless and 2 in 1 Mobility Devices, WCCF Tech, 2014,
http://wccftech.com/intel-14nm-core-m-broadwell-y-processors-detailed/
[187]: Cutress I., Intel Releases Broadwell-U: New SKUs, up to 48 EUs and Iris 6100, AnandTech,
Jan. 5 2015, http://www.anandtech.com/show/8814/intel-releases-broadwell-u-new-
skus-up-to-48-eus-and-iris-6100/4
[189]: Intel Z97 Chipset Platform Diagram, http://www.intel.com/content/www/us/en/chipsets/
performance-chipsets/z97-chipset-diagram.html
[188]: Cutress I., Intel Launches Five 47W Laptop Broadwell SKUs, AnandTech, June 2 2015,
http://www.anandtech.com/show/9326/intel-launches-five-47w-laptop-broadwell-skus
References (22)
[190]: Detalles de los procesadores Intel “Skylake-S” (6° Gen), Taringa, March 2 2015,
http://www.taringa.net/posts/info/18522818/Detalles-de-los-procesadores-Intel-
Skylake-S-6-Gen.html

## Slide 306
[191]: Nguyen C., Intel's Skylake expected to bring stamina and speed to your laptop,
Techradar, 2015, http://www.techradar.com/news/computing-components/processors/
intel-s-skylake-processors-expected-to-bring-stamina-and-speed-to-your-laptop-1300173
[192]: Shilov A., Intel ‘Skylake’ launch schedule revealed: CPUs to arrive in August, Kit Guru,
May 21 2015, http://www.kitguru.net/components/cpu/anton-shilov/complete-intel-
skylake-launch-schedule-revealed-chips-to-be-showcased-in-august/
[193]: Novakovic N., Intel’s 2015 Roadmap Conundrum: Tick-Tock is Not a Swiss Clock, VR World,
May 31 2015, http://www.vrworld.com/2015/05/31/intels-2015-roadmap-conundrum-
tick-tock-is-not-a-swiss-clock/
[194]: Mujtaba H., Intel 14nm Kaby Lake “Skylake Refresh” Platform Detailed – Launching in
2H 2016, 256 MB eDRAM H-Series and 91W K-Series Unveiled, WCCF Tech, 2015,
http://wccftech.com/intel-14nm-kaby-lake-haswell-refresh-platform-detailed-launching-
2h-2016-256-mb-edram-hseries-91w-kseries-unveiled/#ixzz3hczeTsOH
References (23)
[196]: Blythe D., Technology Insight: Next Generation Intel Processor Graphics Architecture
Code Name Skylake, SPCS003, IDF15, San Francisco, Aug. 2015
[195]: Gianos C., Intel Xeon Processor E5-2600 v3 Product Family Architectural Overview ,
Nov. 16 2014
[197]: Kanter D., Intel’s Ivy Bridge Graphics Architecture, Real World Technologies, April 22 2012,
http://www.realworldtech.com/ivy-bridge-gpu/2/
[198]: Rotem E., Intel Architecture, Code Name Skylake, Deep Dive: A New Architecture to Manage
Power Performance and Energy Efficiency, IDF15, San Francisco, Aug. 2015

## Slide 307
[199]: Junkins S., The Compute Architecture of Intel Processor Graphics Gen7.5, Aug. 1 2014,
https://software.intel.com/sites/default/files/managed/f3/13/Compute_Architecture_of_
Intel_Processor_Graphics_Gen7dot5_Aug2014.pdf
[200]: Mandelblat J., Technology Insight: Intel’s Next Generation Microarchitecture, Code Name
Skylake, IDF15, San Francisco, Aug. 2015
[201]: Bright P., The many tricks Intel Skylake uses to go faster and use less power, Ars Technica,
Aug. 19 2015, http://arstechnica.com/information-technology/2015/08/the-many-
tricks-intel-skylake-uses-to-go-faster-and-use-less-power/
[202]: Cutress I., The Intel Skylake Mobile and Desktop Launch, with Architecture Analysis,
AnandTech, Sept. 1 2015, http://www.anandtech.com/show/9582/intel-skylake-mobile-
desktop-launch-architecture-analysis
References (24)
[203]: Chester E., Intel Skylake review: Core i7-6700K and Core i5-6600K review, Trusted Reviews,
Aug. 5 2015, http://www.trustedreviews.com/intel-skylake-review-core-i7-6700k-and-
core-i5-6600k-review#O6vSUh2MV2ptOwqm.99
[204]: Torres A., 4th Generation Intel Core Processor Family, Press Briefing, Spring 2013
[205]: Wikipedia, Haswell (microarchitecture),
https://en.wikipedia.org/wiki/Haswell_(microarchitecture)