## Slide 1
Dezső Sima
Intel’s Core family - TOCK lines
Core 2 to Skylake
October 2016
Vers. 1.3.2

## Slide 2
Contents
1. Introduction
2. The Core 2 line
3. The Nehalem line
4. The Sandy Bridge line
5. The Haswell line
6. The Skylake line
7. The Kaby Lake line
8. References

## Slide 3
1. Introduction
Notes: 3

## Slide 4: 1. Introduction (1)
The evolution of Intel’s basic Core family
Figure 1.1: Intel’s Tick-Tock development model (Based on [1])
1. Introduction
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
1. gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
Skylake
New
Microarchi.
14 nm
TOCK
6. gen.

## Slide 5
Basic architectures | Basic architectures and their shrinks
Pentium 4 (Prescott) | 2005 90 nm Pentium 4 2006 65 nm Pentium 4
Core 2 | 2006 65 nm Core 2 2007 45 nm Penryn
Nehalem | 2008 45 nm Nehalem 2010 32 nm Westmere
Sandy Bridge | 2011 32 nm Sandy Bridge 2012 22 nm Ivy Bridge
Haswell | 2013 22 nm Haswell 2014 14 nm Broadwell
Skylake | 2015 14 nm Skylake 14 nm Kaby Lake ? 10 nm Cannonlake
1. Introduction (2)
Basic microarchitectures and their related shrinks
Considered from the Pentium 4 Prescott (the third core of Pentium 4) on.

## Slide 6: 1. Introduction (3a)
Power density (W/cm2) in Intel's Pentium 4 family

## Slide 7: 1. Introduction (3b)
Recognition of the impact of rising power density (W/cm2) in Intel's
processors at the ISSCC 2001 (P. Gelsinger, Intel)

## Slide 8: 1. Introduction (3c)
Introduction and withdrawal of Intel's P4 family

## Slide 9: 1. Introduction (3d)
Intel's apology for cancelling the Power 4 family [220]
During an interview on stage at Gartner Group’s Fall Symposium/IT Expo in Orlando Intel’s
then Chief Executive Officer Craig Barrett got down on his knees.
In front of an audience of about 7000 information-technology professionals, Barrett asked their
forgiveness for the Santa Clara company latest product slip up, the cancellation of its 4 GHz
Pentium 4 family.
Picture: Oct. 2004 Intel's CEO on his knees to apologize for cancelling the Pentium 4 family [220]

## Slide 10
Changing the design paradigm to cope with raising dissipation
In 2003 Intel shifted the focus of their processor development from the pure performance goal
to the aspect of performance per watt, as stated in a slide from 4/2006, see below.
Figure 1.3: Intel’s plan to develop their manufacturing technology and processor lines
revealed at a shareholder’s meeting back in 4/2006 [74]
1. Introduction (3e)

## Slide 11
High performance/power
(e.g. GFLOPS/Watt)
Traditional processors
Tablets and smartphones
Low power
(Watt)
(Number of operating hours)
With the advent of mobile devices (about 2006) a new design paradigm arose for those devices.
Mobile devices require long operating hours i.e. low power consumption, this is contrast to the
design paradigm of traditional processors, as indicated below.
1. Introduction (4)
Changing the design paradigm for mobile processors

## Slide 12: 1. Introduction (5)
Key requirements for low power microarchitectures
Low processor clock frequency
Narrow microarchitecture
Key requirements for low power microarchitectures

## Slide 13: 1. Introduction (6)
2005
2007
2010
2009
(A9 replacement
for low-end
devices)
32-bit
Example: Width of ARM’s 32-bit CPUs used in most tablets and smartphones [10]
a) Low power CPUs need narrow microarchitectures

## Slide 14: 1. Introduction (7)
By contrast:
Intel’s and AMD’s recent processor lines
aims at high performance/power (in terms of GFLOPS/Watt)
accordingly
have 4-wide microarchitectures, as the next example shows:
64-bit
Example: Width of Intel’s Core 2 to Haswell processors underlying servers to laptops [10]

## Slide 15: 1. Introduction (8)
Consequences for Intel and AMD-1
Intel’s and AMD’s traditional microarchitectures are not suited for mobile devices.
Both Intel and AMD conceived, designed and introduced new, narrow (e.g. 2-wide) low-power microarchitectures.

## Slide 16: 1. Introduction (9a)
Emergence of Intel’s Atom line aiming for tablets and smartphones (Based on [2])
2008
2-wide
in-order
4-wide
out-of-order
2-wide
in order
2-wide
out-of-order

## Slide 17: 1. Introduction (9b)
Worldwide market share of smartphone and tablet application processors in 2015
(based on revenue) [217]
Smartphone application processors worldwide market share 2015 (revenue) | 
Qualcomm (USA) | 42 %
Apple (USA) | 21 %
MediaTek (Taiwan) | 19 %
Samsung (S. Korea) | 
Spreadtrum (China) | 
Tablet application processors worldwide market share 2015 (revenue) | 
Apple (USA) | 31 %
Qualcomm (USA) | 16 %
Intel (USA) | 14 %
MediaTek (Taiwan) | 
Samsung (S. Korea) | 
[Source: Related press releases of Strategy Analytics]

## Slide 18: 1. Introduction (9c)
Intel's withdrawal from the smartphone and mobil market [216]
In 4/2016 Intel announced their withdrawal from the mobil market.
Intel's statement says []:
"I can confirm that the changes included canceling the Broxton platform as
well as SoFIA 3GX, SoFIA LTE and SoFIA LTE2 commercial platforms
to enable us to move resources to products that deliver higher returns and
advance our strategy.
These changes are effective immediately."
At the same time Intel laid off about 12000 employees (~ 11 % of their
workforce).

## Slide 19: 1. Introduction (9d)
Evolution of AMD’s basic architectures
2014
4/2014
2-wide
out-of-order
2-wide
out-of-order
2-wide
out-of-order
4-wide
out-of-order

## Slide 20: 1. Introduction (9e)
Cancellation of AMD's Cat line in 2015
The last core of AMD's Cat line was the Puma+ core (launched in 6/2015 in the
Carrizo-L APU).
In AMD's 2016 Mobility roadmap there is no sign of an APU powered by the
Puma+ core or a derivative of a core belonging to the Cat line.
Instead AMD places emphasis on the Zen architecture to be launched in 2017.

## Slide 21
b) Low power CPUs need low base clock frequencies
High base clock frequency
(typically 2-4 GHz)
Traditional CPUs
Mobile CPUs
Relative low base clock frequency
(typically 1-2 GHz)
( D = const x fc x V2, in addition higher fc requires about linearly higher higher V)
1. Introduction (10)

## Slide 22
TDP (W) | No. of cores | Graphics | No. of graphics EUs | eDRAM | Base frequency (GHz)
4.5 | 2 | HD 515 | 18 | -- | 1.2
15 | 2 | HD 540 | 48 | 64 MB | 2.2
15 | 2 | HD 520 | 24 | -- | 2.6
28 | 2 | HD 550 | 48 | 64 MB | 3.3
35 | 4 | HD 530 | 24 | -- | 2.8
45 | 4 | HD 530 | 24 | -- | 2.9
65 | 4 | HD 530 | 24 | -- | 3.4
91 | 4 | -- | -- | -- | 4.2
Example: The max. base frequency of Skylake models resulting in different TDPs and
configurations (Based on data from [202])
Note that low TDP can be achieved first of all by reducing the core frequency and limiting
the computer resources (cores, GPU EUs) provided.
1. Introduction (11)

## Slide 23: 1. Introduction (12)
Figure : Overview of Intel’s Tick-Tock model (Based on [3])
New microarch.,
64-bit
New microarch.: 4-wide core,
128-bit SIMD FX/FP EUs,
shared L2 , no HT
11/2007
01/2006
90nm
130nm
TICK TOCK
2 YEARS
2 YEARS
2 YEARS
65nm
TICK Pentium 4 / Cedar Mill
TOCK Core 2
2 YEARS
New microarch.
New microarch.,
hyperthreading (HT)
Pentium 4 /Northwood
TICK TOCK
TICK TOCK
Pentium 4 /Prescott
Pentium 4 /Willamette
07/2006
11/2008
New microarch.: 256-bit (FP) AVX,
ring bus, integr. GPU
11/2000
01/2002
02/2004
Key new features of the ISP
and the microarchitecture
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
180nm
256-bit( FX) AVX2,
L4 cache (discrete eDRAM), FIVR
06/2013
09/2014
Shared Virtual Memory
08/2015
ISP,
Memory Side $ (eDRAM), No FIVR
In package integr. GPU
14nm
2 YEARS
TICK Broadwell
TOCK Skylake
New microarch.: integrated MC, QPI,
(inclusive) L3, HT
Intel’s Tick-Tock model for the P4 and Core lines

## Slide 24: 1. Introduction (12b)
Figure : Overview of Intel’s Tick-Tock model (Based on [3])
New microarch.,
64-bit
New microarch.: 4-wide core,
128-bit SIMD FX/FP EUs,
shared L2 , no HT
11/2007
01/2006
90nm
130nm
TICK TOCK
2 YEARS
2 YEARS
2 YEARS
65nm
TICK Pentium 4 / Cedar Mill
TOCK Core 2
2 YEARS
New microarch.
New microarch.,
hyperthreading (HT)
Pentium 4 /Northwood
TICK TOCK
TICK TOCK
Pentium 4 /Prescott
Pentium 4 /Willamette
07/2006
11/2008
New microarch.: 256-bit (FP) AVX,
ring bus, integr. GPU
11/2000
01/2002
02/2004
Key new features of the ISP
and the microarchitecture
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
180nm
256-bit( FX) AVX2,
L4 cache (discrete eDRAM), FIVR
06/2013
09/2014
Shared Virtual Memory
08/2015
ISP,
Memory Side $ (eDRAM), No FIVR
In package integr. GPU
14nm
2 YEARS
TICK Broadwell
TOCK Skylake
New microarch.: integrated MC, QPI,
(inclusive) L3, HT
Intel’s Tick-Tock model for the P4 and Core lines

## Slide 25: 1. Introduction (12c)
Figure : Overview of Intel’s Tick-Tock model (Based on [3])
Clock gating, PECI,
Platform Thermal Control by
3. party controller
11/2007
01/2006
90nm
130nm
TICK TOCK
2 YEARS
2 YEARS
2 YEARS
65nm
TICK Pentium 4 / Cedar Mill
TOCK Core 2
2 YEARS
Pentium 4 /Northwood
TICK TOCK
TICK TOCK
Pentium 4 /Prescott
Pentium 4 /Willamette
07/2006
11/2008
Turbo Boost 2.0
11/2000
01/2002
02/2004
Key new features
in power management
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
180nm
FIVR
06/2013
09/2014
08/2015
Speed Shift Technology,
Duty Cycle control, No FIVR
14nm
2 YEARS
TICK Broadwell
TOCK Skylake
Integrated Power Gates, PCU,
Turbo Boost
Intel’s Tick-Tock model for the P4 and Core lines
EDAT
2. gen. FIVR
Clock gating

## Slide 26: 1. Introduction (13)
Per Generation
Cumulative
Pentium M Dothan
Core 2
Penryn
NHM (w/o SMT)
WSM
SNB
IVB
HSW
BRW
1.8
1.7
1.6
1.5
1.4
1.3
1.1
1.2
1
2
1.9
20%
18%
16%
14%
12%
10%
8%
6%
4%
2%
0%
24%
22%
SKL
Single thread IPC in Intel’s basic architectures (Based on [195])
Note that Intel raised IPC in the Core family only less then 2-times in about 10 years.

## Slide 27: 1. Introduction (14)
Servers
Recent main product categories of Intel
Smartphones
Tablets
Atom lines
Xeon lines
(X86/Itanium)
Desktops/Laptops
(Client computing)
Core lines
(Basic architectures)
Atom lines
(+ LP Core models)
Recent main product categories of Intel and underlying processor lines

## Slide 28
Designation of the platform | Platform topology | Processor | Technology | Max. no. of cores (nC) | Year of introduction | Processor socket | MCH/PCH | Highest mem./ speed grade | No. of mem. channels (nM)
Anchor Creek | Off-die MC | Pentium D | 90 nm | 2x1 | 5/2005 | LGA 775 | 945-955 | DD2-667 | 2
Bridge Creek |  | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
Salt Creek |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series (Bearlake) | DDR3-1067 | 2
Boulder Creek |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series (Eaglelake) | DDR3-1067 | 2
Kings Creek | On-die MC | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series (Ibex Peak) | DDR3-1333 | 2
 |  | Westmere (Clarkdale) | 32 nm | 2C+G | 1/2010 | LGA 1156 | 5 Series (Ibex Peak) |  | 
 |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | LGA 1155 | 6 series (Cougar Point) | DDR3-1333 | 2
Sugar Bay |  |  |  |  |  |  |  |  | 
 |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 | LGA 1155 | 7 series (Panther Point) | DDR3-1600 | 2
 |  | Haswell | 22 nm | 4C+G | 6/2013 | LGA 1155 | 8 Series (Lynx Point) | DDR3-1600 | 2
 |  | Haswell refresh | 22 nm |  | 5/2014 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1666 | 
 |  | Broadwell | 14 nm |  | 6/2015 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1866 | 
 |  | Skylake | 14 nm | 4C+G | 8/2015 | LGA 1151 | Series (Sunrise Point) | DDR4-2133 | 2
Intel’s Core-based mainstream DT platforms
1. Introduction (15a)

## Slide 29
Designation of the platform | Platform topology | Processor | Technology | Max. no. of cores (nC) | Year of introduction | Processor socket | MCH/PCH | Highest mem./ speed grade | No. of mem. channels (nM)
Anchor Creek | Off-die MC | Pentium D | 90 nm | 2x1 | 5/2005 | LGA 775 | 945-955 | DD2-667 | 2
Bridge Creek |  | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
Salt Creek |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series (Bearlake) | DDR3-1067 | 2
Boulder Creek |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series (Eaglelake) | DDR3-1067 | 2
Kings Creek | On-die MC | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series (Ibex Peak) | DDR3-1333 | 2
 |  | Westmere (Clarkdale) | 32 nm | 2C+G | 1/2010 | LGA 1156 | 5 Series (Ibex Peak) |  | 
 |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | LGA 1155 | 6 series (Cougar Point) | DDR3-1333 | 2
Sugar Bay |  |  |  |  |  |  |  |  | 
 |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 | LGA 1155 | 7 series (Panther Point) | DDR3-1600 | 2
 |  | Haswell | 22 nm | 4C+G | 6/2013 | LGA 1155 | 8 Series (Lynx Point) | DDR3-1600 | 2
 |  | Haswell refresh | 22 nm |  | 5/2014 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1666 | 
 |  | Broadwell | 14 nm |  | 6/2015 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1866 | 
 |  | Skylake | 14 nm | 4C+G | 8/2015 | LGA 1151 | Series (Sunrise Point) | DDR4-2133 | 2
Max. number of cores
1. Introduction (15b)

## Slide 30
Designation of the platform | Platform topology | Processor | Technology | Max. no. of cores (nC) | Year of introduction | Processor socket | MCH/PCH | Highest mem./ speed grade | No. of mem. channels (nM)
Anchor Creek | Off-die MC | Pentium D | 90 nm | 2x1 | 5/2005 | LGA 775 | 945-955 | DD2-667 | 2
Bridge Creek |  | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
Salt Creek |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series (Bearlake) | DDR3-1067 | 2
Boulder Creek |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series (Eaglelake) | DDR3-1067 | 2
Kings Creek | On-die MC | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series (Ibex Peak) | DDR3-1333 | 2
 |  | Westmere (Clarkdale) | 32 nm | 2C+G | 1/2010 | LGA 1156 | 5 Series (Ibex Peak) |  | 
 |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | LGA 1155 | 6 series (Cougar Point) | DDR3-1333 | 2
Sugar Bay |  |  |  |  |  |  |  |  | 
 |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 | LGA 1155 | 7 series (Panther Point) | DDR3-1600 | 2
 |  | Haswell | 22 nm | 4C+G | 6/2013 | LGA 1155 | 8 Series (Lynx Point) | DDR3-1600 | 2
 |  | Haswell refresh | 22 nm |  | 5/2014 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1666 | 
 |  | Broadwell | 14 nm |  | 6/2015 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1866 | 
 |  | Skylake | 14 nm | 4C+G | 8/2015 | LGA 1151 | Series (Sunrise Point) | DDR4-2133 | 2
Number of memory channels
1. Introduction (15c)

## Slide 31
Designation of the platform | Platform topology | Processor | Technology | Max. no. of cores (nC) | Year of introduction | Processor socket | MCH/PCH | Highest mem./ speed grade | No. of mem. channels (nM)
Anchor Creek | Off-die MC | Pentium D | 90 nm | 2x1 | 5/2005 | LGA 775 | 945-955 | DD2-667 | 2
Bridge Creek |  | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
Salt Creek |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series (Bearlake) | DDR3-1067 | 2
Boulder Creek |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series (Eaglelake) | DDR3-1067 | 2
Kings Creek | On-die MC | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series (Ibex Peak) | DDR3-1333 | 2
 |  | Westmere (Clarkdale) | 32 nm | 2C+G | 1/2010 | LGA 1156 | 5 Series (Ibex Peak) |  | 
 |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | LGA 1155 | 6 series (Cougar Point) | DDR3-1333 | 2
Sugar Bay |  |  |  |  |  |  |  |  | 
 |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 | LGA 1155 | 7 series (Panther Point) | DDR3-1600 | 2
 |  | Haswell | 22 nm | 4C+G | 6/2013 | LGA 1155 | 8 Series (Lynx Point) | DDR3-1600 | 2
 |  | Haswell refresh | 22 nm |  | 5/2014 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1666 | 
 |  | Broadwell | 14 nm |  | 6/2015 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1866 | 
 |  | Skylake | 14 nm | 4C+G | 8/2015 | LGA 1151 | Series (Sunrise Point) | DDR4-2133 | 2
Platform topology
1. Introduction (15d)

## Slide 32
Designation of the platform | Platform topology | Processor | Technology | Max. no. of cores (nC) | Year of introduction | Processor socket | MCH/PCH | Highest mem./ speed grade | No. of mem. channels (nM)
Anchor Creek | Off-die MC | Pentium D | 90 nm | 2x1 | 5/2005 | LGA 775 | 945-955 | DD2-667 | 2
Bridge Creek |  | Core 2 | 65 nm | 2C | 6/2006 | LGA 775 | 945-975 | DDR2-800 | 2
Salt Creek |  | Core 2 Quad | 65 nm | 2x2C | 6/2007 | LGA 775 | 3 Series (Bearlake) | DDR3-1067 | 2
Boulder Creek |  | Penryn | 45 nm | 2x2C | 6/2008 | LGA 775 | 4 Series (Eaglelake) | DDR3-1067 | 2
Kings Creek | On-die MC | 2. G. Nehalem (Lynnfield) | 45 nm | 4C | 9/2009 | LGA 1156 | 5 Series (Ibex Peak) | DDR3-1333 | 2
 |  | Westmere (Clarkdale) | 32 nm | 2C+G | 1/2010 | LGA 1156 | 5 Series (Ibex Peak) |  | 
 |  | Sandy Bridge | 32 nm | 2C/4C+G | 1/2011 | LGA 1155 | 6 series (Cougar Point) | DDR3-1333 | 2
Sugar Bay |  |  |  |  |  |  |  |  | 
 |  | Ivy Bridge | 22 nm | 4C +G | 4/2012 | LGA 1155 | 7 series (Panther Point) | DDR3-1600 | 2
 |  | Haswell | 22 nm | 4C+G | 6/2013 | LGA 1155 | 8 Series (Lynx Point) | DDR3-1600 | 2
 |  | Haswell refresh | 22 nm |  | 5/2014 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1666 | 
 |  | Broadwell | 14 nm |  | 6/2015 | LGA 1150 | 9 Series (Wild Cat Point) | DDR3-1866 | 
 |  | Skylake | 14 nm | 4C+G | 8/2015 | LGA 1151 | Series (Sunrise Point) | DDR4-2133 | 2
Memory speed up to
1. Introduction (15e)

## Slide 33: 1. Introduction (16)
Key features of the evolution of Intel’s Core-based mainstream DT platforms
Their core count rose soon (already in 2007) to 4 and remain at this figure.
Two memory channels are used to connect memory.
Memory is connected up to the Penryn via the MCH thereafter immediately via the processor.
In a 10 year period memory speed rose about three times.

## Slide 34: 1. Introduction (17a)
Intel’s Core based Extreme Edition (E-Series) DT platforms
The Extreme Edition lines (E-lines) aim at high performance desktops for hardcore gamers
and graphics enthusiasts.

## Slide 35
Intel’s Core based Extreme Edition (E-Series) DT platforms
1. Introduction (17b)
Processor | Techn. | Date of intro. | Max. no. of cores | Platform topology | Highest mem./ speed | PCIe lanes | No. of mem. channels | MCH | Processor socket
1. G. Nehalem EE | 45 nm | 11/2008 | 4C | On-die MC | DDR3-1067 | 36 PCIe 2.0 on the X58 | 3 | X58 (Tylersburg) | LGA 1366
Westmere-EE | 32 nm | 3/2010 | 6C |  |  |  |  |  | LGA 1366
Sandy Bridge-E | 32 nm | 11/2011 | 6C |  | DDR3-1600 | 40 PCIe 2.0 on the die | 4 | X79 (Patsburg) | LGA 2011
Ivy Bridge-E | 22 nm | 9/2013 | 6C |  | DDR3-1866 | 40 PCIe 3.0 on the die | 4 |  | LGA 2011
Haswell-E | 14 nm | 8/2014 | 8C |  | DDR4-2133 |  | 4 | X99 (Wellsburg) | LGA 2011-3
Broadwell-E | 14 nm | 5/2016 | 10C |  | DDR4-2400 |  | 4 | X99 (Wellsburg) | LGA 2011-3

## Slide 36
Number of cores up to
1. Introduction (17c)
Processor | Techn. | Date of intro. | Max. no. of cores | Platform topology | Highest mem./ speed | PCIe lanes | No. of mem. channels | MCH | Processor socket
1. G. Nehalem EE | 45 nm | 11/2008 | 4C | On-die MC | DDR3-1067 | 36 PCIe 2.0 on the X58 | 3 | X58 (Tylersburg) | LGA 1366
Westmere-EE | 32 nm | 3/2010 | 6C |  |  |  |  |  | LGA 1366
Sandy Bridge-E | 32 nm | 11/2011 | 6C |  | DDR3-1600 | 40 PCIe 2.0 on the die | 4 | X79 (Patsburg) | LGA 2011
Ivy Bridge-E | 22 nm | 9/2013 | 6C |  | DDR3-1866 | 40 PCIe 3.0 on the die | 4 |  | LGA 2011
Haswell-E | 14 nm | 8/2014 | 8C |  | DDR4-2133 |  | 4 | X99 (Wellsburg) | LGA 2011-3
Broadwell-E | 14 nm | 5/2016 | 10C |  | DDR4-2400 |  | 4 | X99 (Wellsburg) | LGA 2011-3

## Slide 37
Number of memory channels
1. Introduction (17d)
Processor | Techn. | Date of intro. | Max. no. of cores | Platform topology | Highest mem./ speed | PCIe lanes | No. of mem. channels | MCH | Processor socket
1. G. Nehalem EE | 45 nm | 11/2008 | 4C | On-die MC | DDR3-1067 | 36 PCIe 2.0 on the X58 | 3 | X58 (Tylersburg) | LGA 1366
Westmere-EE | 32 nm | 3/2010 | 6C |  |  |  |  |  | LGA 1366
Sandy Bridge-E | 32 nm | 11/2011 | 6C |  | DDR3-1600 | 40 PCIe 2.0 on the die | 4 | X79 (Patsburg) | LGA 2011
Ivy Bridge-E | 22 nm | 9/2013 | 6C |  | DDR3-1866 | 40 PCIe 3.0 on the die | 4 |  | LGA 2011
Haswell-E | 14 nm | 8/2014 | 8C |  | DDR4-2133 |  | 4 | X99 (Wellsburg) | LGA 2011-3
Broadwell-E | 14 nm | 5/2016 | 10C |  | DDR4-2400 |  | 4 | X99 (Wellsburg) | LGA 2011-3

## Slide 38
Number of PCIe lanes
1. Introduction (17e
Processor | Techn. | Date of intro. | Max. no. of cores | Platform topology | Highest mem./ speed | PCIe lanes | No. of mem. channels | MCH | Processor socket
1. G. Nehalem EE | 45 nm | 11/2008 | 4C | On-die MC | DDR3-1067 | 36 PCIe 2.0 on the X58 | 3 | X58 (Tylersburg) | LGA 1366
Westmere-EE | 32 nm | 3/2010 | 6C |  |  |  |  |  | LGA 1366
Sandy Bridge-E | 32 nm | 11/2011 | 6C |  | DDR3-1600 | 40 PCIe 2.0 on the die | 4 | X79 (Patsburg) | LGA 2011
Ivy Bridge-E | 22 nm | 9/2013 | 6C |  | DDR3-1866 | 40 PCIe 3.0 on the die | 4 |  | LGA 2011
Haswell-E | 14 nm | 8/2014 | 8C |  | DDR4-2133 |  | 4 | X99 (Wellsburg) | LGA 2011-3
Broadwell-E | 14 nm | 5/2016 | 10C |  | DDR4-2400 |  | 4 | X99 (Wellsburg) | LGA 2011-3

## Slide 39: 1. Introduction (18)
They provide typically
more cores
more memory channels (to appropriately service more processing resources)
more PCIe lanes (either on the PCH or on the die)
than the standard desktop platform,
they do not provide integrated graphics, as it is assumed that the installation is intended
to provide high quality graphics by attaching multiple discrete graphics cards.
they are unlocked, nevertheless
They have a high power consumption of 130 to 150 W.
Key features of Intel’s Core-based Extreme Edition lines (E-lines)

## Slide 40: 1. Introduction (19)
Server platforms classified according to the number of processors supported
DP (2S)
server platforms
Server platforms
Platforms for more than four servers
2- processor server platforms
(2-socket server platforms)
MP (4S)
server platforms
4-processor server platforms
(4-socket server platforms)
(Server platforms for
more than four sockets)
Uniprocessor server platforms
(UP-server platforms)
1-processor server platforms
(1-socket server platforms)
Multiprocessor server platforms
Server platforms supporting more than one processor
(Multi-socket server platforms)

## Slide 41
Platform | Platform topology | Date of intro. | Processor | Technology | Core count (up to) | No. and speed of memory channels/socket | Kind of connecting memory Socket
Truland MP | SMP w/dual FSBs | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 90 nm | 1C | 1x DDR2-400/socket | 4 serial channels (IMI) via MCH LGA 604
 |  | 11/2005 | Xeon 7000 (Paxville MP) | 90 nm | 2x1C |  | 
 |  | 8/2006 | Xeon 7100 (Tulsa) | 65 nm | 2C |  | 
Caneland | SMP w/Quad FSBs | 9/2007 | Xeon 7200 Tigerton DC (Core 2) | 65 nm | 2C | 1x DDR2-667/socket (FB-DIMM) | 4 serial FB-DIMM channels via MCH LGA 604
 |  | 9/2007 | Xeon 7300 Tigerton QC (Core 2) | 65 nm | 2x2C |  | 
 |  | 9/2008 | Xeon 7400 (Dunnington) (Penryn) | 45 nm | 6C |  | 
Boxboro-EX | NUMA fully connect. | 3/2010 | Nehalem-EX (Xeon 7500/ (Beckton) | 45 nm | 8C | 8x DDR3-1067/socket | 4 serial channels (SMI) /processor LGA 1567
 |  | 4/2011 | Westmere-EX (E7-4800) | 32 nm | 10C |  | 
Brickland | NUMA fully connect. | 2/2014 | Ivy Bridge-EX (E7-4800 v2) | 22 nm | 15C | 8x DDR3-1600/socket | 4 parallel channels (SMI2)/processor LGA-2011-1
 |  | 5/2015 | Haswell-EX (E7-4800 v3) | 22 nm | (14C) 18C | 8x DDR4-1866/socket | 
Intel’s Core-based MP server platforms
1. Introduction (20)

## Slide 42
Platform | Platform topology | Date of intro. | Processor | Technology | Core count (up to) | No. and speed of memory channels/socket | Kind of connecting memory Socket
Truland MP | SMP w/dual FSBs | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 90 nm | 1C | 1x DDR2-400/socket | 4 serial channels (IMI) via MCH LGA 604
 |  | 11/2005 | Xeon 7000 (Paxville MP) | 90 nm | 2x1C |  | 
 |  | 8/2006 | Xeon 7100 (Tulsa) | 65 nm | 2C |  | 
Caneland | SMP w/Quad FSBs | 9/2007 | Xeon 7200 Tigerton DC (Core 2) | 65 nm | 2C | 1x DDR2-667/socket (FB-DIMM) | 4 serial FB-DIMM channels via MCH LGA 604
 |  | 9/2007 | Xeon 7300 Tigerton QC (Core 2) | 65 nm | 2x2C |  | 
 |  | 9/2008 | Xeon 7400 (Dunnington) (Penryn) | 45 nm | 6C |  | 
Boxboro-EX | NUMA fully connect. | 3/2010 | Nehalem-EX (Xeon 7500/ (Beckton) | 45 nm | 8C | 8x DDR3-1067/socket | 4 serial channels (SMI) /processor LGA 1567
 |  | 4/2011 | Westmere-EX (E7-4800) | 32 nm | 10C |  | 
Brickland | NUMA fully connect. | 2/2014 | Ivy Bridge-EX (E7-4800 v2) | 22 nm | 15C | 8x DDR3-1600/socket | 4 parallel channels (SMI2)/processor LGA-2011-1
 |  | 5/2015 | Haswell-EX (E7-4800 v3) | 22 nm | (14C) 18C | 8x DDR4-1866/socket | 
1. Introduction (21)
a) The rate of rising core counts in Intel's MP servers -1

## Slide 43: 1. Introduction (22)
Core count
2006
2008
2010
2012
2014
2016
Year
7000
(90 nm)
7300
(65 nm)
7400
(45 nm)
Nehalem-EX
(45 nm)
Westmere-EX
(32 nm)
Ivy-Bridge-EX
(22 nm)
Broadwell-EX
(14 nm)
*
*
*
*
*
2
4
8
16
32
24
10
6
15
*
*
~2x/4 years
~2x/2 years
a) The rate of rising core counts in Intel's MP servers -2

## Slide 44: 1. Introduction (23)
Thermal sensors
2 cores
2 cores
2 cores
4 MB LLC
4 MB LLC
4 MB LLC
4 MB LLC
3 MB MLC
3 MB MLC
3 MB MLC
Tags
Tags
Data pad
Address pad
Figure: Die plot of the 6-core Xeon 7400 MP (Dunnington) [215]
The reason why the rate of rising core counts slowed down: Optimisation in utilizing
the die area among cores and caches
8 MB L3
3 MB L2/2 cores

## Slide 45: 1. Introduction (24)
The core count of MP servers rose up to about 6 cores more or less according to Moore’s
rule, thereafter the growth rate slowed down to doubling about every four years,
as indicated in the previous Figure.
a) The rate of rising core counts in Intel's MP servers -3

## Slide 46
Platform | Platform topology | Date of intro. | Processor | Technology | Core count (up to) | No. and speed of memory channels/socket | Kind of connecting memory Socket
Truland MP | SMP w/dual FSBs | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 90 nm | 1C | 1x DDR2-400/socket | 4 serial channels (IMI) via MCH LGA 604
 |  | 11/2005 | Xeon 7000 (Paxville MP) | 90 nm | 2x1C |  | 
 |  | 8/2006 | Xeon 7100 (Tulsa) | 65 nm | 2C |  | 
Caneland | SMP w/Quad FSBs | 9/2007 | Xeon 7200 Tigerton DC (Core 2) | 65 nm | 2C | 1x DDR2-667/socket (FB-DIMM) | 4 serial FB-DIMM channels via MCH LGA 604
 |  | 9/2007 | Xeon 7300 Tigerton QC (Core 2) | 65 nm | 2x2C |  | 
 |  | 9/2008 | Xeon 7400 (Dunnington) (Penryn) | 45 nm | 6C |  | 
Boxboro-EX | NUMA fully connect. | 3/2010 | Nehalem-EX (Xeon 7500/ (Beckton) | 45 nm | 8C | 8x DDR3-1067/socket | 4 serial channels (SMI) /processor LGA 1567
 |  | 4/2011 | Westmere-EX (E7-4800) | 32 nm | 10C |  | 
Brickland | NUMA fully connect. | 2/2014 | Ivy Bridge-EX (E7-4800 v2) | 22 nm | 15C | 8x DDR3-1600/socket | 4 parallel channels (SMI2)/processor LGA-2011-1
 |  | 5/2015 | Haswell-EX (E7-4800 v3) | 22 nm | (14C) 18C | 8x DDR4-1866/socket | 
b) The rate of rising memory transfer rates in Intel’s MP servers -1
1. Introduction (25)

## Slide 47
*
*
*
*
Transfer rate (MT/s)
50
100
500
Year
03
05
01
02
04
06
07
08
1000
3000
200
2000
~ 2*/4 years
DDR2
533
DDR2
667
DDR2 800
DDR3
1600
09
11
2010
12
13
15
DDR3
1067
2000

14
*
*
DDR3
1333
*
DDR4/2133
DDR3/1866
*
*
*
DDR
333
~ 2*/8 years
DDR
266
b) The rate of rising memory transfer rates in Intel’s MP servers -2
x
x
x
x
x
*
DDR
400
DDR2
667
DDR3
1600
DDR3
1866
DDR
400
DDR3
1067
DT
MP
1. Introduction (26)

## Slide 48: 1. Introduction (27)
In the course of the evolution of MP servers memory transfer rate rose slower than
core count, for DDR2 memories it doubled roughly every four years.
But after DDR3 memory emerged the growth rate of memory transfer speed slowed down
to doubling rougly every eight years due to the higher complexity of this technology,
as the next Figure shows.
b) The rate of rising memory transfer rates in Intel’s MP servers -3

## Slide 49: 1. Introduction (28)
We point out that the requested memory bandwidth of a platform based on a multicore
processor needs to be proportional with the core count, since every core may run
independently from each other.
Since the memory transfer rate raises slower than the core count, the resulting memory
bandwidth deficiency needs to be compensated by increasing the number of memory
channels provided by the MP platform.
c) The inherent widening memory gap

## Slide 50: 1. Introduction (29)
It can be shown that an n-core MP server needs to have approximately √n memory channels
per socket for preserving the per core memory bandwidth over server generations.
This is the reason why the number of memory channels rose rapidly from 1 per socket
to 8 per socket.
d) The need for more memory channels for higher core counts -1

## Slide 51
Platform | Platform topology | Date of intro. | Processor | Technology | Core count (up to) | No. and speed of memory channels/socket | Kind of connecting memory Socket
Truland MP | SMP w/dual FSBs | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 90 nm | 1C | 1x DDR2-400/socket | 4 serial channels (IMI) via MCH LGA 604
 |  | 11/2005 | Xeon 7000 (Paxville MP) | 90 nm | 2x1C |  | 
 |  | 8/2006 | Xeon 7100 (Tulsa) | 65 nm | 2C |  | 
Caneland | SMP w/Quad FSBs | 9/2007 | Xeon 7200 Tigerton DC (Core 2) | 65 nm | 2C | 1x DDR2-667/socket (FB-DIMM) | 4 serial FB-DIMM channels via MCH LGA 604
 |  | 9/2007 | Xeon 7300 Tigerton QC (Core 2) | 65 nm | 2x2C |  | 
 |  | 9/2008 | Xeon 7400 (Dunnington) (Penryn) | 45 nm | 6C |  | 
Boxboro-EX | NUMA fully connect. | 3/2010 | Nehalem-EX (Xeon 7500/ (Beckton) | 45 nm | 8C | 8x DDR3-1067/socket | 4 serial channels (SMI) /processor LGA 1567
 |  | 4/2011 | Westmere-EX (E7-4800) | 32 nm | 10C |  | 
Brickland | NUMA fully connect. | 2/2014 | Ivy Bridge-EX (E7-4800 v2) | 22 nm | 15C | 8x DDR3-1600/socket | 4 parallel channels (SMI2)/processor LGA-2011-1
 |  | 5/2015 | Haswell-EX (E7-4800 v3) | 22 nm | (14C) 18C | 8x DDR4-1866/socket | 
1. Introduction (23)
d) The need for more memory channels for higher core counts -2

## Slide 52: 1. Introduction (31)
Finally, we note that the basic platform topology has changed with the Nehalem processor
from SMP to NUMA, as indicated next.
e) Changing the basic platform topology of MP platforms from SMP to NUMA -1

## Slide 53: 1. Introduction (32)
SMPs
(Symmetrical MultiProcessor)
Basic platform topologies of multiprocessors
classified according to their memory architecture
NUMAs
Multiprocessors (Multi socket system)
with Non-Uniform Memory Access
Multiprocessors (Multi socket system)
with Uniform Memory Access (UMA)
Typical examples
Processor
MCH
ICH
FSB
Processor
E.g. DDR2-533
ESI
E.g. DDR3-1333
Processor
IOH1
QPI
QPI
ICH
ESI
QPI
E.g. DDR3-1333
Processor
All processors access main memory by the same
mechanism, (e.g. by individual FSBs and an MCH).
A particular part of the main memory can be accessed
by each processor immediately, other parts remotely.
1ICH: I/O hub
ESI: Enterprise System Interface
e) Changing the basic platform topology of MP platforms from SMP to NUMA -2

## Slide 54
Platform | Platform topology | Date of intro. | Processor | Technology | Core count (up to) | No. and speed of memory channels/socket | Kind of connecting memory Socket
Truland MP | SMP w/dual FSBs | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 90 nm | 1C | 1x DDR2-400/socket | 4 serial channels (IMI) via MCH LGA 604
 |  | 11/2005 | Xeon 7000 (Paxville MP) | 90 nm | 2x1C |  | 
 |  | 8/2006 | Xeon 7100 (Tulsa) | 65 nm | 2C |  | 
Caneland | SMP w/Quad FSBs | 9/2007 | Xeon 7200 Tigerton DC (Core 2) | 65 nm | 2C | 1x DDR2-667/socket (FB-DIMM) | 4 serial FB-DIMM channels via MCH LGA 604
 |  | 9/2007 | Xeon 7300 Tigerton QC (Core 2) | 65 nm | 2x2C |  | 
 |  | 9/2008 | Xeon 7400 (Dunnington) (Penryn) | 45 nm | 6C |  | 
Boxboro-EX | NUMA fully connect. | 3/2010 | Nehalem-EX (Xeon 7500/ (Beckton) | 45 nm | 8C | 8x DDR3-1067/socket | 4 serial channels (SMI) /processor LGA 1567
 |  | 4/2011 | Westmere-EX (E7-4800) | 32 nm | 10C |  | 
Brickland | NUMA fully connect. | 2/2014 | Ivy Bridge-EX (E7-4800 v2) | 22 nm | 15C | 8x DDR3-1600/socket | 4 parallel channels (SMI2)/processor LGA-2011-1
 |  | 5/2015 | Haswell-EX (E7-4800 v3) | 22 nm | (14C) 18C | 8x DDR4-1866/socket | 
1. Introduction (33)
e) Changing the basic platform topology of MP platforms from SMP to NUMA -3

## Slide 55
Intel Core generation | Graphics generation | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Westmere | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 7th | HD 2500 | GT1 | 1 (6 EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Evolution of main features of Intel’s graphics families (based on [174]) -1
1. Introduction (34)

## Slide 56
Intel Core generation | Graphics generation | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Westmere | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 7th | HD 2500 | GT1 | 1 (6 EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Evolution of main features of Intel’s graphics families (based on [174]) -2
1. Introduction (35)

## Slide 57
Intel Core generation | Graphics generation | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Westmere | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 7th | HD 2500 | GT1 | 1 (6 EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Evolution of main features of Intel’s graphics families (based on [174]) -3
1. Introduction (36)

## Slide 58: 1. Introduction (37)
Example: A slice of the graphics unit of Haswell (including 20 EUs) [199]

## Slide 59
Intel Core generation | Graphics generation | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Westmere | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 7th | HD 2500 | GT1 | 1 (6 EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Evolution of main features of Intel’s graphics families (based on [174])
1. Introduction (38)

## Slide 60
Intel Core generation | Graphics generation | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Westmere | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 7th | HD 2500 | GT1 | 1 (6 EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Evolution of main features of Intel’s graphics families (based on [174]) -4
1. Introduction (39)

## Slide 61
Intel Core generation | Graphics generation | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Westmere | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 7th | HD 2500 | GT1 | 1 (6 EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Evolution of main features of Intel’s graphics families (based on [174]) -5
1. Introduction (40)

## Slide 62: 1. Introduction (41)
Key features of the evolution of Intel’s integrated graphics families
Intel’s graphics implementations are subdivided into
graphics generations (5th to 9th) and
graphics technology levels (GT1-GT4).
Graphics generations are bound to the basic architectures.
The graphics technology levels indicate the number of graphics slices (replicable sets of
graphics EUs) within each graphics generation.
The number of graphics EUs is increasing more or less according to Moore’s rule
(from 12 in 2010 to 72 in 2015).
With the Haswell basic architecture graphics became eDRAM support (first 64 MB
then 128 MB)
There is continuous support of newer versions of graphics APIs and of OpenCL.

## Slide 63: 1. Introduction (42)
Graphics performance increase of subsequent Core generations [196]
Skylake
Broadwell
Haswell
Ivy Bridge
Sandy Bridge

## Slide 64
2. The Core 2 line
2.1 Introduction
2.2 Major innovations of the Core 2 line
2.4 Die plot of the Core 2
2.5 Overview of Core 2 based processor lines
2.3 Performance leadership change between
Intel and AMD achieved by the Core 2
Notes: 64

## Slide 65
2.1 Introduction
Notes: 65

## Slide 66: 2.1 Introduction (1)
2.1 Introduction-1
The next line became based primarily on the Pentium M – Intel’s first mobile line
since for its designs dissipation reduction was a key issue.
(The Pentium M line was a 32-bit line with 3 subsequent cores, designed at
Intel’s Haifa Research and Development Center) thus the Core 2 was developed also there.
The Pentium 4 line was cancelled due to unmanageable high dissipation figures
of its third core (the 90 nm Prescott core)
(caused primarily by the design philosophy of the line
that preferred clock frequency over core efficiency for increasing performance).
The Haifa team had no experience with multithreading.
The Core microarchitecture does not support multithreading.
For the development of the next processor line dissipation became the key design issue.

## Slide 67: 2.1 Introduction (2)
Figure : Intel’s Tick-Tock development model (Based on [1])
Figure 4.1.1: Intel’s Tick-Tock development model (Based on [1])
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
1. gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
Skylake
New
Microarchi.
14 nm
TOCK
6. gen.
The Core 2 is Intel’s 1. generation new microarchitecture, it is using 65 nm line width.
First delivered in 6/2006.
2.1 Introduction-2

## Slide 68: 1. Introduction (12)
Figure : Overview of Intel’s Tick-Tock model (Based on [3])
New microarch.,
64-bit
New microarch.: 4-wide core,
128-bit SIMD FX/FP EUs,
shared L2 , no HT
11/2007
01/2006
90nm
130nm
TICK TOCK
2 YEARS
2 YEARS
2 YEARS
65nm
TICK Pentium 4 / Cedar Mill
TOCK Core 2
2 YEARS
New microarch.
New microarch.,
hyperthreading (HT)
Pentium 4 /Northwood
TICK TOCK
TICK TOCK
Pentium 4 /Prescott
Pentium 4 /Willamette
07/2006
11/2008
New microarch.: 256-bit (FP) AVX,
ring bus, integr. GPU
11/2000
01/2002
02/2004
Key new features of the ISP
and the microarchitecture
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
180nm
256-bit( FX) AVX2,
L4 cache (discrete eDRAM), FIVR
06/2013
09/2014
Shared Virtual Memory
08/2015
ISP,
Memory Side $ (eDRAM), No FIVR
In package integr. GPU
14nm
2 YEARS
TICK Broadwell
TOCK Skylake
New microarch.: integrated MC, QPI,
(inclusive) L3, HT
The Core 2 line

## Slide 69
2.2 Major innovations of the Core 2 line
2.2.1 4-wide core
2.2.3 Smart L2 cache
2.2.4 Innovations in power management
2.2.2 128-bit SIMD and FP units
Notes: 69

## Slide 70: 2.2.1 4-wide core (1)
2.2 Major innovations of the Core 2 line
2.2.1 4-wide core
This is the key benefit of the Core 2 family.
By contrast
both Intel’s previous Pentium 4 family and AMD’s K8 have only 3-wide cores,
as the next Figures show.
It means 4-wide front end and retire unit.

## Slide 71: 2.2.1 4-wide core (2)
Figure 2.2.1.1: Block diagram of Intel’s Core 2 microarchitecture [4]

## Slide 72: 2.2.1 4-wide core (3)
Figure 2.2.1.2: Block diagram of Intel’s Pentium 4 microarchitecture [5]
Retire width: 3 instr./cycle

## Slide 73: 2.2.1 4-wide core (4)
Figure 2.2.1.3: Block diagram of AMD’s K8 microarchitecture[4]

## Slide 74: 2.2.2 128-bit wide SIMD and FP units (1)
a) Overview of the x86 ISA extensions in Intel’s processor lines
2.2.2 128-bit wide SIMD and FP units
They aim at providing enhanced media support.

## Slide 75: 2.2.2 128-bit wide SIMD and FP units (2)
Advanced Encryption Standard
Advanced Vector Extension
Fused Multiply-Add instr.
Streaming SIMD Extensions
MultiMedia eXtensions
Northwood (Pentium 4)
Ivy Bridge
Pentium III
Pentium 4
Core 2
Overview of Intel’s x86 ISA extensions (based on [18])

## Slide 76: 2.2.2 128-bit wide SIMD and FP units (3)
Norhwood
Northwood (Pentium4)
Northwood (Pentium4)
8 MM registers (64-bit),
aliased on the FP Stack registers
8 XMM registers (128-bit)
16 XMM registers (128-bit)
16 YMM registers (256-bit)
Ivy Bridge
Pentium MMX
Pentium 4
Core 2
Pentium III
Register spaces provided by Intel’s x86 ISA extensions (based on [18])

## Slide 77: 2.2.2 128-bit wide SIMD and FP units (4)
Illustration of the available SIMD register spaces of the MMX to SSE3/SSSE3 ISA
extensions in 32- and 64-bit ISAs [162]

## Slide 78: 2.2.2 128-bit wide SIMD and FP units (5)
Norhwood
Northwood (Pentium4)
128-bit FX, FP SIMD with
32/16/8-bit FX, 32-bit FP ops.
Support of MM/3D
DSP-oriented FP enhancements,
enhanced thread manipulation
Diverse arithmetic enhancements
64-bit FX SIMD with
32/16/8-bit operands (ops)
Support of MM
128-bit FX, FP SIMD with
64/32/16/8-bit FX, 64/32-bit FP,
Support for MPEG-2, video, MP3
Media acceleration
(video encoding, MM, gaming)
Accelerated string/text manip.,
appl. targeted acceleration
Accelerated encription operations
256-bit FP SIMD with
64/32-bit FP
Ivy Bridge
Pentium III
Pentium 4
Core 2
Intel’s x86 ISA extensions - the operations introduced (based on [18])

## Slide 79: 2.2.2 128-bit wide SIMD and FP units (6)
SSSE3 provide 32 instructions (represented by 14 mnemonics) to accelerate computations on
packed integers.
These include:
Overview of the Supplemental Streaming SIMD Extension (SSSE3) of the Core 2 ISA
[161]
• Twelve instructions that perform horizontal addition or subtraction operations (operations
on adjacent numbers.
• Six instructions that evaluate absolute values.
• Two instructions that perform multiply and add operations and speed up the evaluation
of dot products.
• Two instructions that accelerate packed-integer multiply operations and produce integer
values with scaling.
• Two instructions that perform a byte-wise, in-place shuffle according to the second
shuffle control operand.
• Six instructions that negate packed integers in the destination operand if the signs of the
corresponding element in the source operand is less than zero.
• Two instructions that align data from the composite of two operands.

## Slide 80: 2.2.2 128-bit wide SIMD and FP units (7)
Northwood (Pentium 4)
1 full + 1 simple (moves/stores)
64-bit FP/SSE EUs
2 x 128-bit FP EUs +
3 x 128-bit SSE EUs
256-bit SSE EUs
2 x 32-bit FX MMX EUs
2 x 32-bit MMX,
2 x 32-bit SSE EUs
Ivy Bridge
Pentium III
Pentium 4
Core 2
SIMD execution resources in Intel’s basic processors (based on [18])

## Slide 81: 2.2.2 128-bit wide SIMD and FP units (8)
The Core 2 has 128-bit wide and more FP and SSE execution units than Pentium 4 or AMD’s K8,
as detailed below.
b) Contrasting the number of 128-bit wide execution units in Intel’s Pentium 4, Core 2
and AMD’s K8 -1
The next Figure demonstrates it.
Core 2
two 128-bit FP units
three 128-bit SSE units
Pentium 4
single 64-bit FP/SSE unit
single 64-bit FP/SSE move unit
AMD K8
two 64-bit FP/SSE units
single 64-bit FP/SSE move unit

## Slide 82: 2.2.2 128-bit wide SIMD and FP units (9)
FP/SSE
K8 Execution Units
b) Contrasting the number of 128-bit wide execution units in Intel’s Pentium 4, Core 2
and AMD’s K8 -2 [159], [160]

## Slide 83: 2.2.2 128-bit wide SIMD and FP units (10)
Core 2’s achieved performance boost for gaming apps vs. AMD’s Athlon 64 FX60 [13]

## Slide 84: 2.2.3 Shared L2 cache (1)
Pentium 4-based DCs
Core 2-based DCs
2.2.3 Shared L2 cache
Core1
Core2
L2 Cache
L2 Cache
Core1
Core2
L2 Cache
Figure 2.2.3.1: Core’s shared L2 cache vs. Pentium 4’s private L2 caches
Private
Shared
In the Core 2 Intel makes use a shared L2 cache instead of private L2 caches and designates it
as smart L2 cache, as shown below.

## Slide 85: 2.2.3 Shared L2 cache (2)
Benefits of shared caches vs. private caches
Dynamic cache allocation to the individual cores
Data sharing (no replicated data)
+ 2x bandwidth to L1 caches.

## Slide 86: 2.2.3 Shared L2 cache (3)
Drawbacks of shared caches
Shared caches combine memory access patterns
Reduce the efficiency of hardware prefetching vs private caches.
Choice between shared and private caches
Design decision depending on
whether benefits or drawbacks dominate as far as performance is concerned.
Trend
Core 2 prefers a shared L2 cache
Nehalem prefers private L2 caches
POWER5 prefers shared L2 cache
POWER6 prefers private L2 caches
This trend is due to the fact that efficient data prefetching became more important than
dynamic cache allocation or data sharing.

## Slide 87: 2.2.3 Shared L2 cache (4)
Intel’s first hardware prefetcher appeared subsequently in the Pentium 4 family,
associated with the L2 cache (one instruction and one data prefetcher (11/2000).
Principle of operation of the L2 hardware prefetcher
it monitors data access patterns and prefetches data automatically into the L2 cache,
it attempts to stay 256 bytes ahead of the current data access location,
the prefetcher remembers the history of cache misses to detect concurrent,
independent data streams that it tries to prefetch ahead of its use.
Remarks
Intensive use of hardware prefetchers -1 [9]
Intel’s first on-die L2 cache debuted only about two years earlier (8/1998),
in the second core of the Pentium II based Celeron line (called the Mendocino core,
built on 250 nm technology, with an L2 size of 128 KB)1,2.
1 The first Celeron model debuted in 4/1998, it was the low cost alternative to Pentium II,
and was designated as Cavington.
It was manufactured on 250 nm, run at 266 MHz, did not include an L2 cache and had 7.5 mtrs.
The second core of the Celeron line was launched in 8/1998 already with an L2 cache, run
at 266 and 300 MHz and incorporated 19,2 mtrs.
2Note: The debut of L2 was corrected in 29/10/2014.

## Slide 88: 2.2.3 Shared L2 cache (5)
8 prefetchers in the two-core processor
2 data and 1 L1 instruction prefetchers per core,
able to handle multiple simultaneous patterns.
2 prefetchers in the L2 cache
tracking multiple access patterns per core.
Intensive use of hardware prefetchers -2 [11]

## Slide 89: 2.2.3 Shared L2 cache (6)
Figure 2.2.3.2: Hardware prefetchers within the Core 2 microarchitecture [11]
Hardware prefetchers in the Core 2 microarchitecture

## Slide 90: 2.2.4 Innovations in power management (1)
2.2.4 Innovations in power management
Shutting off not needed functional units of the processor
Platform Thermal Control

## Slide 91: 2.2.4 Innovations in power management (2)
Green units not needed
for the given operation,
they can be shut off.
Shutting off not needed functional units of the processor by clock gating [11]

## Slide 92: 2.2.4 Innovations in power management (3)
Platform Thermal Control [11], [20]
Digital
Thermal Sensors
(DTS) on the dies,
instead of
analog diodes,
providing
digital data,
scanned by
dedicated logic.
(Platform Environment Control Interface)
A single wire proprietary interface with
transfer rates of 2 kbit/s-2 Mbit/s)
DTSs report the difference between the
current temperature and the throttle point,
at which the processor reduces speed.
PECI

## Slide 93: 2.2.4 Innovations in power management (4)
Possible solution for the Platform Thermal Control Manager [88]
Figure 2.2.4.1: The aSC7621 hardware monitor with fan control and PECI from Andigilog
(Remote Sensor)
(Remote Sensor
CPU/Graphics)
(ASIC (Application Specific IC/Microcontroller)

## Slide 94
2.3 Performance leadership change between Intel and AMD achieved by the Core 2
Notes: 94

## Slide 95: 2.3 Performance leadership change between Intel and AMD (1)
AMD’s K8-based processors became the performance leader, first of all on the DP and MP
server market, where the 64-bit direct connect architecture has clear benefits
vs Intel’s 32-bit Pentium 4 based processors using shared FSBs to connect processors
to north bridges.
integrated memory controllers and
high speed point-to-point serial buses (the HyperTransport bus)
used to connect processors to processors and processors to south bridges.
Performance leadership change between Intel and AMD achieved by the Core 2
In 2003 AMD introduced their K8-based processors implementing
the 64-bit x86 ISA and
the direct connect architecture concept, that includes

## Slide 96: 2.3 Performance leadership change between Intel and AMD (2)
Figure 2.3.1: DP web server performance comparison: AMD Opteron 248 vs. Intel Xeon 2.8 [6]
Example 1: DP web-server performance comparison (2003)

## Slide 97: 2.3 Performance leadership change between Intel and AMD (3)
“In the extensive benchmark tests under Linux Enterprise Server 8 (32 bit as well as 64 bit), the AMD Opteron made a good impression.
Especially in the server disciplines, the benchmarks (MySQL, Whetstone, ARC 2D, NPB, etc.) show quite clearly that the Dual Opteron puts the Dual Xeon in its place”.
Example 2: Summary assessment of extensive benchmark tests contrasting
dual Opterons vs dual Xeons (2003) [7]

## Slide 98: 2.3 Performance leadership change between Intel and AMD (4)
two 128-bit FP units and three 128-bit SSE units compared to
This situation has completely changed in 2006 when Intel introduced their Core 2
microarchitecture,
Intel regained performance leadership vs AMD.
This and further enhancements of the Core microarchitecture, detailed subsequently,
resulted in record breaking performance figures.
a 4-wide front-end and retire unit compared to the 3-wide K8,
The Core 2 has
two 64-bit FP/SSE units and a single 64-bit FP/SSE move unit available in the K8.

## Slide 99: 2.3 Performance leadership change between Intel and AMD (5)
Webserver Performance |  |  |  |  | 
 | MSI K2-102A2M Opteron 275 | MSI K2-102A2M Opteron 280 | Opteron 280 vs. Opteron 275 | Extrapolated Opteron 3 GHz | Xeon 5160 3 GHz
Jsp - Peak | 144 | 154 | 7% | 182 | 230
AMP - Peak | 984 | 1042 | 6% | 1178 | 1828
Jsp: Java Server Page performance
AMP: Apache/MySQL/PHP
Example: DP web-server performance comparison (2006)
Figure 2.2.1.8: DP web server performance comparison:
AMD Opteron 275/280 vs. Intel Xeon 5160 [8]
Remark
Both web-server benchmark results were published from the same source (AnandTech)

## Slide 100
2.4 Die plot of the Core 2
Notes: 100

## Slide 101: 2.4 Die plot of the Core 2 (1)
143 mm2
291 mtrs
2.4 Die plot of the Core 2 [163]

## Slide 102
2.5 Overview of Core 2 based processor lines
Notes: 102

## Slide 103: 2.5 Overview of Core 2 based processor lines (1)
2.5 Overview of Core 2 based processor lines
Servers
DP-Servers
MP-Servers
51xx, 2C Woodcrest, 6/2006
53xx, 2x2, Clowertown, (2xWoodcrest) 11/2006
72xx, 2C, Tigerton DC, (2xMP-enhanced SC Woodcrest) 9/2007
73xx, 2x2C, Tigerton QC, (2xMP-enhanced DC Woodcrest) 9/2007
UP-Servers
30xx, 2C, Conroe, 9/2006
30xx, 2C, Allendale 1/2007
32xx, 2x2C, Kentsfield (2xConroe) 1/2007
Mobiles
T5xxx/T7xxx, 2C ,Merom 8/2006
Based on [43]
Desktops
E6xxx/E4xxx, 2C, Core 2 Duo, (Conroe) 7/2006
X6800 Core 2 Extreme, 2C, (Conroe) 7/2006
E6xxx/E4xxx, Core 2 Duo, 2C, (Allendale) 1/2007
Q6xxx Core 2 Quad, 2x2C (Kentsfield) (2xConroe) 1/2007
QX6xxx Core 2 Extreme Quad, 2x2C, (Kentsfield XE) 11/2006

## Slide 104
3. The Nehalem line
3.1 Introduction to the 1. generation Nehalem line
(Bloomfield)
3.2 Major innovations of the 1. gen. Nehalem line
3.3 Major innovations of the 2. gen. Nehalem line
(Lynnfield)
Notes: 104

## Slide 105
3.1 Introduction to the 1. generation Nehalem line (Bloomfield)
Notes: 105

## Slide 106: 3.1 Introduction to the 1. generation Nehalem line (Bloomfield) (1)
3.1 Introduction to the 1. generation Nehalem line (Bloomfield)
Developed at Hillsboro, Oregon, at the site where the Pentium 4 was designed.
Experiences with HT
Nehalem became a multithreaded design.
The design effort took about five years and required thousands of engineers
(Ronak Singhal, lead architect of Nehalem) [37].
(Core i7-9xx (Bloomfield)) 4C in 11/2008
First implementation of the Nehalem microarchitecture appeared in the desktop segment
Figure : Intel’s Tick-Tock development model (Based on [1])
Figure 4.1.1: Intel’s Tick-Tock development model (Based on [1])
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
1. gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
Skylake
New
Microarchi.
14 nm
TOCK
6. gen.

## Slide 107: 1. Introduction (12)
Figure : Overview of Intel’s Tick-Tock model (Based on [3])
New microarch.,
64-bit
New microarch.: 4-wide core,
128-bit SIMD FX/FP EUs,
shared L2 , no HT
11/2007
01/2006
90nm
130nm
TICK TOCK
2 YEARS
2 YEARS
2 YEARS
65nm
TICK Pentium 4 / Cedar Mill
TOCK Core 2
2 YEARS
New microarch.
New microarch.,
hyperthreading (HT)
Pentium 4 /Northwood
TICK TOCK
TICK TOCK
Pentium 4 /Prescott
Pentium 4 /Willamette
07/2006
11/2008
New microarch.: 256-bit (FP) AVX,
ring bus, integr. GPU
11/2000
01/2002
02/2004
Key new features of the ISP
and the microarchitecture
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
180nm
256-bit( FX) AVX2,
L4 cache (discrete eDRAM), FIVR
06/2013
09/2014
Shared Virtual Memory
08/2015
ISP,
Memory Side $ (eDRAM), No FIVR
In package integr. GPU
14nm
2 YEARS
TICK Broadwell
TOCK Skylake
New microarch.: integrated MC, QPI,
(inclusive) L3, HT
The Nehalem line

## Slide 108: 3.1 Introduction to the 1. generation Nehalem line (Bloomfield) (3)
1. generation Nehalem processors
Nehalem lines
Desktops
Servers
DP-Servers
55xx Gainestown (Nehalem-EP) 4C 3/2009
Core i7-9xx (Bloomfield) 4C 11/2008
UP-Servers
35xx Bloomfield 4C 3/2009
Mobiles
1Jasper forest: Embedded UP or DP server
Based on [44]
2. generation Nehalem processors
Desktops
Servers
DP-Servers
C55xx Jasper forest1 2C/4C 2/2010
Core i7-8xx (Lynnfield) 4C 9/2009
Core i5-7xx (Lynnfield) 4C 9/2009
UP-Servers
34xx Lynnfield 4C 9/2009
C35xx Jasper forest1 4C 2/2010
Core i7-9xxM Clarksfield 4C 9/2009
Core i7-8xxQM Clarksfield 4C 9/2009
Core i7-7xxQM Clarksfield 4C 9/2009
Mobiles

## Slide 109: 3.1 Introduction to the 1. generation Nehalem line (Bloomfield) (4)
Die shot of the Bloomfield chip [45]
Die shot of the 1. generation Nehalem desktop processor (Bloomfield) [45]
The Bloomfield die has two QPI bus controllers, in spite of the fact that they are not needed
for the desktop part.
In the Bloomfield die one of the controllers is simply not activated [45], whereas both are
active in the DP alternative (Gainestown).
Both the desktop oriented Bloomfield chip and the DP server oriented Gainestown chip have
the same layout.
Note
(8 MB)

## Slide 110
3.2 Major innovations of the 1. generation Nehalem line
3.2.1 Integrated memory controller
3.2.2 QuickPath Interconnect bus (QPI)
3.2.3 New cache architecture
3.2.5 Enhanced power management
3.2.6 New socket
3.2.4 Simultaneous Multithreading
Notes: 110

## Slide 111: 3.2 Major innovations of the 1. generation Nehalem line (1)
Integrated memory controller
(Section 3.2.1)
QuickPath Interconnect bus (QPI)
(Section 3.2.2)
New cache architectureure
(Section 3.2.3)
• Simultaneous Multithreading (SMT)
(Section 3.2.4)
SSE 4.2 ISA extension
(Not detailed)
Enhanced power management
(Section 3.2.5)
Advanced virtualization
(Not detailed)
New socket
(Section 3.2.6)
3.2 Major innovations of the 1. generation Nehalem line [54]
Figure 3.2.1: Die photo of the Bloomfield/Gainestown chip
(8 MB)
The Major incentive for designing the microarchitecture of Nehalem: support of 4 cores.
4 cores need however twice as much bandwidth as dual core processors, such as the Core 2.
Two memory channels used for dual core processors are more or less the limit attachable to
the north bridge due to physical and electrical limitations.
Consequently, to provide enough bandwidth for 4 cores, a new memory design was necessary.
Major innovations of the 1. generation 4-core Nehalem line

## Slide 112: 3.2.1 Integrated memory controller (1)
3.2.1 Integrated memory controller
Traditional system architectures, as shown below for the Core 2 Duo processor, can
implement not more than two high speed memory channels connected to the MCH.
These system architectures can provide enough bandwidth only for up to dual core processors.
Figure: Core 2 Duo based
platform [166]

## Slide 113: 3.2.1 Integrated memory controller (2)
The need for integrated memory controller in a dual processor QC Nehalem platform
Main features
3 channels per socket
Up to 3 DIMMs per channel (impl. dependent)
DDR3-800, 1066, 1333,…
Supports both RDIMMs and UDIMMs (impl. dependent)
Figure 3.2.1.1: Integrated memory controller of Nehalem [33]
Nehalem-EP (Efficient Performance):
Designation of the server line
n cores
n times higher memory bandwidth need

## Slide 114: 3.2.1 Integrated memory controller (3)
Benefits and drawback of integrated memory controllers
Low memory access latency
important for memory intensive apps.
Drawback of integrated memory controllers
Processor becomes memory technology dependent
For an enhanced memory solution (e.g. for increased memory speed)
a new processor modification is needed.
Benefits

## Slide 115: 3.2.1 Integrated memory controller (4)
Local memory access
Remote memory access
Most multi-socket platforms use NUMA
Remote memory access latency ~ 1.7 x longer than local memory access latency
Demands a fast processor-to-processor interconnection to relay memory traffic (QPI)
Operating systems have to modify memory allocation strategies + related APIs
Figure 3.2.1.2: Non Uniform Memory Access (NUMA) in multi-socket servers [1]
Non Uniform Memory Access (NUMA)
It is a consequence of using integrated memory controllers in case of multi-socket servers

## Slide 116: 3.2.1 Integrated memory controller (5)
Memory latency comparison: Nehalem vs Penryn [1]
Harpertown: Quad-Core Penryn based server (Xeon 5400 series)

## Slide 117: 3.2.1 Integrated memory controller (6)
Remark
Intel’s Timna – a forerunner to integrated memory controllers [34]
Timna (announced in 1999, due to 2H 2000, cancelled in Sept. 2000)
Developed in Intel’s Haifa Design and Development Center.
Low cost microprocessor with integrated graphics and memory controller
(for Rambus DRAMs).
Due to design problems and lack of interest from many vendors,
Intel finally cancelled Timna in Sept. 2000.
Figure 3.2.1.4: The low cost (<600 $) Timna PC [40]

## Slide 118: 3.2.1 Integrated memory controller (7)
Point of attaching memory
Attaching memory to the processor(s)
Attaching memory to the MCH
POWER4 (2C) (2001)
POWER5 (2C) (2005)
and subsequent POWER families
Montecito (2C) (2006)
Opteron server lines (2C) (2003)
and all subsequent AMD lines
PA-8800 (2004)
PA-8900 (2005)
and all previous PA lines
Core 2 Duo line (2C) (2006)
and all preceding Intel lines
Core 2 Quad line (2x2C) (2006/2007)
Penryn line (2x2C) (2008)
Nehalem lines (4) (2008)
and all subsequent Intel lines
Examples
Tukwila (4C) (2010)
AMD’s K7 lines (1C) (1999-2003)
UltraSPARC III (2001)
and all subsequent Sun lines
UltraSPARC II (1C) (~1997)
Point of attaching memory

## Slide 119
3.2.2 QuickPath Interconnect bus (QPI) -1
A serial, high speed differential point-to-point interconnect bus, similar to AMD’s
HyperTransport bus, used to connect processors to processors or processors to north bridges.
3.2.2 QuickPath Interconnect bus (QPI) (1)
Its debut is strongly motivated by the introduction of integrated memory controllers.
Formerly designated as the Common System Interface bus (CSI bus).

## Slide 120
Principle of differential interconnections [170]
3.2.2 QuickPath Interconnect bus (QPI) (2)

## Slide 121
3.2.2 QuickPath Interconnect bus (QPI)- 2
Consists of 2 unidirectional links, one in each directions, called the TX and RX
(T for Transmit, R for Receive).
3.2.2 QuickPath Interconnect bus (QPI) (2a)

## Slide 122
16 data
2 protocol
2 CRC
TX Unidirectional link
RX Unidirectional link
Signals of the QuickPath Interconnect bus (QPI bus) [22]
(DDR data transfer)
3.2.2 QuickPath Interconnect bus (QPI) (3)

## Slide 123
QuickPath Interconnect bus (QPI) -3
Each unidirectional link comprises 20 data lanes and a clock lane, with
each lane consisting of a pair of differential signals.
3.2.2 QuickPath Interconnect bus (QPI) (4)
(Lane: Vonalpár)

## Slide 124
LVDS: Low Voltage Differential Signaling LVTTL: Low Voltage TTL
(D)RSL: (Differential) Rambus Signaling Level SSTL: Stub Series Terminated Logic VCM: Common Mode Voltage VREF: Reference Voltage
LVTTL (3.3 V)
FPM/EDO
SDRAM
HI 1.5
TTL (5 V)
FPM/EDO
SSTL
SSTL2 (DDR)
SSTL1.8 (DDR2)
SSTL1.5 (DDR3)
RSL (RDRAM)
FSB
LVDS
PCIe
QPI, DMI, ESI
FB-DIMMs
Smaller voltage swings
DRSL
XDR (data)
Signaling systems used in buses
3.2.2 QuickPath Interconnect bus (QPI) (5)
Signals
Voltage referenced
Single ended
Differential
t
t
VREF
t
S+
S-
VCM
Typ.voltage
swings
600-800 mV
200-300 mV
3.3-5 V
Signaling
system
used in

## Slide 125
QPI based DP server architecture [169] -1
3.2.2 QuickPath Interconnect bus (QPI) (6)
Note
First generation Nehalem (Bloomfielf) supports only DP configurations.

## Slide 126
QPI based MP server architecture [169] -2
3.2.2 QuickPath Interconnect bus (QPI) (7)

## Slide 127
QPI based 8-processor system architecture [169] -3
3.2.2 QuickPath Interconnect bus (QPI) (8)

## Slide 128
QuickPath Interconnect Bus (QPI-bus)
up to 3.2 GHz DDR 2-Byte (Nehalem)
12.8 GB/s in each direction
Fastest FSB
400 MHz QDR 8 Byte
12.8 GB/s bidirectional
HyperTransport Bus (HT-bus)
HT 1.0: 0.8 GHz DDR 2-Byte
3.2 GB/s in each direction
HT 2.0: 1.0 GHz DDR 2-Byte
4.0 GB/s in each direction
HT 3.0: 2.6 GHz DDR 2-Byte
10.4 GB/s in each direction
Max. clock speed and width figures in AMD’s systems
Comparison of the transfer rates of the QPI, FSB and HT buses
DDR: Double Data Rate
HT 3.1: 3.2 GHz DDR 2-Byte
12.8 GB/s in each direction
QDR: Quad Data Rate
3.2.2 QuickPath Interconnect bus (QPI) (9)
up to 4.0 GHz GHz DDR 2-Byte (Sandy Bridge E/EP)
16.0 GB/s in each direction
up to 4.8 GHz GHz DDR 2-Byte (Haswell E/EP)
19.2 GB/s in each direction

## Slide 129: 3.2.3 New cache architecture (1)
2-level cache hierarchy
(Penryn)
3-level cache hierarchy
(Nehalem)
Figure 3.2.3.1: The 3-level cache architecture of Nehalem (based on [1])
32 kB/32 KB
256 KB
Private
4 MB
Shared/
two cores
Up to 8 MB
Inclusive
3.2.3 New cache architecture
L1 Caches
L1 Caches
L2 Cache
Core
Core
Core
Core
L1 Caches
L2 Cache
Core
32 kB/32 KB
L1 Caches
L1 Caches
L2 Caches
L2 Caches
L3 Cache
Note the difference in the L2 cache sizes to the previous generation.

## Slide 130: 3.2.3 New cache architecture (2)
Distinguished features of Nehalem’s cache architecture
The L2 cache is private again rather than shared as in the Core and Penryn processors
Private L2
Shared L2
Pentium 4
Core
Penryn
Nehalem
Assumed reason for returning to the private scheme
Private caches allow a more effective hardware prefetching than shared ones, since
Hardware prefetchers look for memory access patterns.
Private L2 caches have more easily detectable memory access patterns
than shared L2 caches.

## Slide 131: 3.2.3 New cache architecture (3)
Remark
The POWER family had the same evolution path as above
Private L2
Shared L2
POWER4
POWER5
POWER6

## Slide 132: 3.2.3 New cache architecture (4)
The L3 cache is inclusive rather than exclusive
like in a number of competing designs, such as UltraSPARC IV+ (2005), POWER5 (2005),
POWER6 (2007), POWER7 (2010), POWER8 (2014), AMD’s K10-based processors (2007).
Intel’s argumentation for inclusive caches [38]
Inclusive L3 caches prevent L2 snoop traffic for L3 cache misses since
with inclusive L3 caches an L3 cache miss means that the referenced data
doesn’t exist in any core’s L2 caches, thus no L2 snooping is needed.
By contrast, with exclusive L3 caches the referenced data may exist in any
of the L2 caches, thus L2 snooping is required,
as indicated in the next Figure.

## Slide 133: 3.2.3 New cache architecture (5)
It is guaranteed that data is not on die
Core
Core
L1 Caches
L2 Cache
Core
L1 Caches
L1 Caches
L2 Caches
L2 Caches
L3 Cache
L1 Caches
L2 Cache
Core
Core
Core
L1 Caches
L2 Cache
Core
L1 Caches
L1 Caches
L2 Caches
L2 Caches
L3 Cache
L1 Caches
L2 Cache
Core
Inclusive L3
Exclusive L3
Miss
Miss
All other cores must be checked (snooped)!
Benefit of inclusive L3 caches (based on [209])

## Slide 134: 3.2.3 New cache architecture (6)
Benefit of inclusive L3 caches (based on [209])
For higher core numbers L2 snooping becomes a more demanding task and overshadows the
benefits arising from the more efficient cache use of the explicit cache scheme.

## Slide 135: 3.2.3 New cache architecture (7)
Vendor | Model | Core count | L2 MB | Year of intro. |  | Model | Core count | L3 | Year of intro
IBM | POWER3 II | 1C | 16 MB off-chip | 1999 |  | POWER4 | 2C | 32 MB off-chip | 2001
 |  |  |  |  |  | POWER5 | 2C | 36 MB off-chip | 2004
 |  |  |  |  |  | POWER6 | 2C | 32 MB off-chip | 2007
 |  |  |  |  |  | POWER7 | 8C | 8X4MB on-chip | 2010
AMD | K8 Santa Rosa | 2C | 2x1 MB on-chip | 2006 |  | K10 Barcelona | 4C | 2 MB on-chip | 2007
Intel | Penryn | 2C | 6 MB on-chip | 2008 |  | Nehalem | 4C | 8 MB on-chip | 2008
Introduction of L3 caches

## Slide 136
The notion of “Uncore” [1]
3.2.3 New cache architecture (8)

## Slide 137: 3.2.4 Simultaneous Multithreading (SMT) (1)
Figure 3.2.4.1: Simultaneous Multithreading (SMT) of Nehalem [1]
3.2.4 Simultaneous Multithreading (SMT)
Two-way multithreaded ( two threads at the same time)
A 4-wide core is fed more efficiently (from 2 threads).
Hides latency of a single tread.
More performance with low additional die area cost,
May provide significant performance increase on
dedicated applications.
Benefits

## Slide 138: 3.2.4 Simultaneous Multithreading (SMT) (2)
Performance gains achieved by Nehalem’s SMT [1]

## Slide 139: 3.2.5 Enhanced power management (1)
3.2.5 Enhanced power management
Discussed issues
Integrated power gates
Integrated Power Control Unit
Turbo Boost technology

## Slide 140: 3.2.5 Enhanced power management (2)
Power switches
Use of integrated power gates [32]

## Slide 141: 3.2.5 Enhanced power management (3)
Allows to manage the power
of the whole chip as an entity.
Used also for the Turbo Boost Mode
Overview of the Power Control unit [32]

## Slide 142: 3.2.5 Enhanced power management (4)
Forerunner of Nehalem’s Turbo Boost technology in the Penryn
The Penryn core already introduced a less intricate technology for the same purpose,
termed as the (EDAT) Enhanced Dynamic Acceleration Technology that increases
clock frequency only for the mobile platform and in case if one of the two cores is inactive.
EDAT considers a core “active” if it is in ACPI C0 or C1 states, whereas cores in the C3
to C6 ACPI states are considered as “inactive”.
Nehalem’s Turbo Boost technology

## Slide 143: 3.2.5 Enhanced power management (5)
ACPI states (underlying EDAT) [26]
Intelligent
heuristics decides
when enter into.
Passive states
ACPI: Advanced Configuration and Power Interface
An open standard for operating system worked out to enable power management.

## Slide 144: 3.2.5 Enhanced power management (6)
Principle of the operation of Nehalem’s Turbo Boost technology (1)
Nehalem has already a PCU (Power Control Unit) that is aware of the full power dissipation
of the whole package.
If the actual power dissipation is lower than a given limit, called TDP, the PCU increases the
clock frequency of the active cores to raise the performance.
TDP (Thermal Design Power) is the design value, given in W, for the cooling system of the
platform.
TDP is chosen such that it reflects the maximum power consumed by realistic power intensive
applications.
The cooling system (called also thermal solution) has to assure that the chip, more precisely
the junction temperature (Tj) does not exceed a given limit (Tjmax, e.g. 90 oC).

## Slide 145: 3.2.5 Enhanced power management (7)
The Turbo mode uses the power headroom given by the unused TDP limit of the proc. package [52].
Principle of the operation of
Nehalem's Turbo Boost technology (2) [52]

## Slide 146: 3.2.5 Enhanced power management (8)
Note that in Nehalem’s turbo mode all active cores in the processor will operate at the same fc
and voltage.

## Slide 147: 3.2.5 Enhanced power management (9)
Principle of the operation of Nehalem's Turbo Boost technology (3) [51]
The operating system (OS) is responsible for the power management by measuring the actual
workload and instructing the hardware to set fc and Vc accordingly.
idle cores or
a light workload
it will increase the core frequency of the active cores e.g. in steps of 133 MHz, as long as
given limits, e.g. the power consumption of the processor package and the junction
temperatures of the cores remain below the given limits.
When the PCU detects that the given limits become exceeded it will step down clock frequency
in steps of e.g. 133 MHz.
If the OS requests the highest fc and the PCU recognizes that the actual power consumption
of the package is less than the TDP, i.e. there is a power headroom available due to

## Slide 148: 3.2.5 Enhanced power management (10)
To control fc the PCU samples the current power consumption and die temperatures in 5 ms
intervals [53].
Power consumption is determined by monitoring the processor current at its input pin as well
as the associated voltage (Vcc) and calculating the power consumption as a moving average.
The junction temperature of the cores are monitored by DTSs (Digital Thermal Sensors) with
an error of ± 5 % [50].
Assuring that power and temperature values do not exceed specified limits [53], [50]
When the power consumption of the processor or the junction temperature of any core
exceeds the factory configured limits, the PCU automatically steps down core frequency
in increments of e.g. 133 MHz.

## Slide 149: 3.2.5 Enhanced power management (11)
Maximum turbo frequencies are factory configured and kept in an internal register (MSR 1ADH).
E.g. in case of the Core i7-920XM the basic core frequency is 2.0 GHz and the maximum
Turbo frequency is 3.2 GHz, which is 9 frequency bins (9 x 133 MHz) higher than the TDP limited
basic core frequency of 2.0 GHz.
The maximum Turbo Boost frequency [53]

## Slide 150: 3.2.6 New sockets (1)
LGA-775
(Core 2)
LGA-1366
(Bloomfied)
LGA-1156
(Lynnfield)
3.2.6 New sockets [167]

## Slide 151
3.3 Major innovations of the 2. generation Nehalem line (Lynnfield)
Notes: 151

## Slide 152: 3.3 Major innovations of the 2. generation Nehalem line (Lynnfield) (1)
1. generation Nehalem processors
Nehalem lines
Desktops
Servers
DP-Servers
55xx Gainestown (Nehalem-EP) 4C 3/2009
Core i7-9xx (Bloomfield) 4C 11/2008
UP-Servers
35xx Bloomfield 4C 3/2009
Mobiles
1Jasper forest: Embedded UP or DP server
Based on [44]
2. generation Nehalem processors
Desktops
Servers
DP-Servers
C55xx Jasper forest1 2C/4C 2/2010
Core i7-8xx (Lynnfield) 4C 9/2009
Core i5-7xx (Lynnfield) 4C 9/2009
UP-Servers
34xx Lynnfield 4C 9/2009
C35xx Jasper forest1 4C 2/2010
Core i7-9xxM Clarksfield 4C 9/2009
Core i7-8xxQM Clarksfield 4C 9/2009
Core i7-7xxQM Clarksfield 4C 9/2009
Mobiles

## Slide 153: 3.3 Major innovations of the 2. generation Nehalem line (Lynnfield) (2)
3.3 Major innovations of the 2. generation Nehalem line (Lynnfield) (1) [46]
a) The Lynnfield chip is a major redesign of the Bloomfield chip resulting in a cheaper and
more effective two-chip system solution instead of the previous three chip solution.
The Bloomfield based platform (X58 + ICH10 / LGA-1366)
The Lynnfield based platform (P55 / LGA-1156)
b) Further on, whereas the Bloomfield chip is connected to the X58 chipset via the QPI bus,
the Lynnfield chip is connected to the P55 PCH by a DMI interface, like in previous solutions.

## Slide 154
Major innovations of the 2. generation Nehalem line (Lynnfield) (2) [46]
The Bloomfield based platform (X58 + ICH10 / LGA-1366)
The Lynnfield based platform (P55 / LGA-1156)
c) It provides only 16 PCIe 2.0 lanes to attach a graphics card immediately to the processor
rather than to the north bridge as done by 36 lanes in the previous solution.
3.3 Major innovations of the 2. generation Nehalem line (Lynnfield) (3)

## Slide 155: 3.3 Major innovations of the 2. generation Nehalem line (Lynnfield) (4)
Evolution of providing PCIe lanes for graphics

## Slide 156
1x x16 or 2x x8 lanes (DTs)
PCIe lanes provided on the processor
40 configurable lanes (HEDs)
(e.g. 2x x16 + 1x x8 or 4x x8)
PCIe 3.0 lanes
PCIe 2.0 lanes
Type of available PCIe lanes
PCIe 1.0 lanes
Mem.
P
Periph. Contr.
PCIe
2.0
X16/
2x x8
X16/
2x x8
Mem.
P
Periph. Contr.
PCIe
3.0
PCIe 3.0
40
configurable
lanes
Intel 2. gen. Nehalem (Lynnfield) (4C), 2 MCh
with P55 (2009)
Intel Sandy Bridge (4C), 2 MCh with P67 (2011)
Intel Ivy Bridge (4C), 2 MCh with Z77 PCH (2012) to
Skylake (4C), 2 MCh with Z170 PCH (2015)
P55/P67
Z77 to Z170
Intel Ivy Bridge-E (6C), 4 MCh with X79 (2013)
Intel Haswell-E (8C), 4 MCh with X79 (2014)
Main options of providing PCIe lanes on the processor for graphics cards in DT systems
Mem.
P
Periph. Contr.
X79
PCIe 2.0
40
configurable
lanes
Intel Sandy Bridge-E (6C), 4 MCh with X79 (2011)
Mem.
P
Periph. Contr.
X79
3.3 Major innovations of the 2. generation Nehalem line (Lynnfield) (5)
MCh: Memory Channel
(Desktops)
(High-end Desktops (HEDs))

## Slide 157: 3.3 Major innovations of the 2. generation Nehalem line (Lynnfield) (6)
PCIe 3.0
lanes
PCIe 2.0
lanes
Type of available PCIe lanes
PCIe 1.0
lanes
Trend
Evolution of the topology and type of available PCIe lanes for graphics cards
Topology of PCIe lanes provided for graphics cards
PCIe lanes
on both the NB and the SB
PCIe lanes
on the NB
PCIe lanes
on the processor
PCIe lanes
on the PCH
2. G. Nehalem (Lynnfield)
(2009)
Sandy Bridge (2011)
Sandy Bridge-E (2011)
Ivy Bridge (2012)
Ivy-Bridge-E (2013)
Haswell (2013)
Haswell-E (2014) tp
Skylake (2015)

## Slide 158
d) It supports only two DDR3 memory channels instead of three as in the previous solution.
e) Its socket needs less connections (LGA-1156) than the Bloomfield chip (LGA-1366).
All in all the Lynnfield chip is a cheaper and more effective successor of the Bloomfield chip,
aiming primarily for mobiles and desktops.
Major innovations of the 2. generation Nehalem line (Lynnfield) (3) [46]
The Bloomfield based platform (X58 + ICH10 / LGA-1366)
The Lynnfield based platform (P55 / LGA-1156)
3.3 Major innovations of the 2. generation Nehalem line (Lynnfield) (7)

## Slide 160
Bloomfield
(desktop/DP server) []
Second generation: Lynnfield chip (9/2009)
45 nm, 296 mm2, 774 mtrs, LGA-1156) [45] [46] [48]
First generation: Bloomfield chip (11/2008)
(45 nm, 263 mm2, 731 mtrs, LGA-1366)
Die photos of the 1. and 2. gen.
Nehalem desktop chips
[45], [46], [47]
3.3 Major innovations of the 2. generation Nehalem line (Lynnfield) (8)

## Slide 161
4. The Sandy Bridge line
4.1 Introduction
4.2 Major innovations of the Sandy Bridge line vs.
the 1. generation Nehalem line
4.3 Example for a Sandy Bridge based desktop
platform with the H67 chipset
Notes: 161

## Slide 162
4.1 Introduction
Notes: 162

## Slide 163: 4.1 Introduction (1)
Sandy Bridge is Intel’s next new microarchitecture using 32 nm line width.
First delivered in 1/2011.
It is termed also as Intel’s second generation Core processors.
4.1 Introduction
Figure : Intel’s Tick-Tock development model (Based on [1])
Figure 4.1.1: Intel’s Tick-Tock development model (Based on [1])
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
1. gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
Skylake
New
Microarchi.
14 nm
TOCK
6. gen.

## Slide 164: 1. Introduction (12)
Figure : Overview of Intel’s Tick-Tock model (Based on [3])
New microarch.,
64-bit
New microarch.: 4-wide core,
128-bit SIMD FX/FP EUs,
shared L2 , no HT
11/2007
01/2006
90nm
130nm
TICK TOCK
2 YEARS
2 YEARS
2 YEARS
65nm
TICK Pentium 4 / Cedar Mill
TOCK Core 2
2 YEARS
New microarch.
New microarch.,
hyperthreading (HT)
Pentium 4 /Northwood
TICK TOCK
TICK TOCK
Pentium 4 /Prescott
Pentium 4 /Willamette
07/2006
11/2008
New microarch.: 256-bit (FP) AVX,
ring bus, integr. GPU
11/2000
01/2002
02/2004
Key new features of the ISP
and the microarchitecture
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
180nm
256-bit( FX) AVX2,
L4 cache (discrete eDRAM), FIVR
06/2013
09/2014
Shared Virtual Memory
08/2015
ISP,
Memory Side $ (eDRAM), No FIVR
In package integr. GPU
14nm
2 YEARS
TICK Broadwell
TOCK Skylake
New microarch.: integrated MC, QPI,
(inclusive) L3, HT
The Sandy Bridge line

## Slide 165: 4.1 Introduction (3)
Sandy Bridge
Up to 4 cores
(This Section)
Sandy Bridge-E
Up to 6 cores
(Not discussed)
Core i7-3960X EE, 6C, 11/2011
Core i7-3930K, 6C, 11/2011
Core i7-3820, 4C, 11/2011
Desktops
Servers
Mobiles
Core i3-23xxM, 2C, 2/2011
Core i5-24xxM//25xxM, 2C, 2/2011
Core i7-26xxQM/27xxQM/28xxQM, 4C, 1/2011
Core i7 Extreme-29xxXM , 4C, Q1 2011
Core i3-21xx, 2C, 2/2011
Core i5-23xx 4C+G, 1/2011
Core i5/24xx/25xx, 4C+G, 1/2011
Core i7-26xx, 4C+G, 1/2011
Core i7-2700K, 4C+G10/2011
Sandy Bridge-EN/EP
Up to 8 cores
(Not discussed)
Sandy Bridge-EP
(Efficient Performance)
(Socket: LGA 2011)
E5-24xx 4/6/8C, 5/2012
Sandy Bridge-EN
(Entry)
(Socket: LGA 1356)
E5-26xx 4/6/8C, 3/2012
E5-46xx 4/6/8C, 5/2012
DP-Servers
MP-Servers
The Sandy Bridge family
Overview of the Sandy Bridge family
Based on [62] and [63]
Microservers
E3 1220L/1230L/1260L, 2C/4C, 4/2011
UP-Servers
E3 12x0, 4C, 4/2011
E3 12x5, 4C+G, 4/2011
E5-14xx 4/6C, 5/2012
E5-16xx 4/6C, 3/2012
Notes: ridge-ex

## Slide 166: 4.1 Introduction (4)
32K L1D (3 clk)
AVX 256 bit
4 Operands
256 KB L2
(9 clk)
Hyperthreading
AES Instr.
VMX Unrestrict.
20 nm2 / Core
256 KB L2
(9 clk)
256 KB L2
(9 clk)
256 KB L2
(9 clk)
256 KB L2
(9 clk)
256 KB L2
(9 clk)
256 KB L2
(9 clk)
PCIe 2.0
@ 1.0 1.4 GHz
(to L3 connected)
256 b/cycle Ring Architecture
(25 clk)
DDR3-1600
25.6 GB/s
Main functional units of Sandy Bridge [96]
32 nm process / ~225 nm2 die size. 995 mtrs, 85W TDP
8 MB

## Slide 167
4.2 Major innovations of the Sandy Bridge line vs.
the 1. generation Nehalem line
4.2.1 Overview
4.2.2 Extension of the ISA by the 256-bit
AVX instruction set
4.2.3 New microarchitecture of the cores
4.2.4 On die ring interconnect bus
4.2.5 On die graphics unit
4.2.6 Turbo Boost 2.0 technology
Notes: 167

## Slide 168
4.2 Major innovations of the Sandy Bridge line vs. the 2. generation Nehalem line [61]
4.2.1 Overview
4.2.1 Overview (1)
Extension of the ISA by the 256-bit
AVX instruction set (Section 4.2.2)
New microarchitecture for the cores
(Section 4.2.3)
On die ring interconnect bus
(Section 4.2.4)
On-die graphics unit
(Section 4.2.5)
Turbo Boost technology 2.0
(Section 4.2.6)

## Slide 169
4.2.2 Extension of the ISA by the 256-bit AVX instruction set
4.2.2 Extension of the ISA by the AVX instruction set (1)
AVX: Advanced Vector Extensions
In the course of ISA extensions Intel expanded the previous 128-bit SSE SIMD instruction set (introduced with the Pentium III in 1999) by the 256-bit AVX SIMD instruction set, as follows:

## Slide 170
Width of Intel’s subsequent SIMD extensions (Based on [18])
Norhwood
Northwood (Pentium4)
Northwood (Pentium4)
Ivy Bridge
4.2.2 Extension of the ISA by the AVX instruction set (2)
Pentium III
Pentium III
Core 2
128-bit
64-bit
256-bit

## Slide 171
The 256-bit AVX extension
It includes
Extension of the 128-bit wide XMM [0, 15] SIMD register set to the 256-bit YMM [0, 15]
register set.
b) Extension of the 128-bit SSE instruction set.
4.2.2 Extension of the ISA by the AVX instruction set (3)

## Slide 172
Norhwood
Northwood (Pentium4)
Northwood (Pentium4)
8 MM registers (64-bit),
aliased on the FP Stack registers
8 XMM registers (128-bit)
16 XMM registers (128-bit)
16 YMM registers (256-bit)
Ivy Bridge
4.2.2 Extension of the ISA by the AVX instruction set (4)
Pentium III
Pentium III
Core 2
Available register set
Available SIMD register sets in Intel’s subsequent SIMD extensions (Based on [18])

## Slide 173
Extension of the 128-bit wide XMM [0, 15] SIMD register set to the 256-bit
YMM [0, 15] register set [97], [168]
4.2.2 Extension of the ISA by the AVX instruction set (5)

## Slide 174
b) Extension of the 128-bit SSE instruction set
Supported data types [168]
4.2.2 Extension of the ISA by the AVX instruction set (6)
float
float
FX

## Slide 175
Note
AVX doubled only FP vector width, as indicated in the Figure below [97].
4.2.2 Extension of the ISA by the AVX instruction set (7)
AVX doubled FP vector width
and register file width
Doubling peak FLPOPS

## Slide 176
Implementation of AVX -1 [218]
To implement 256-bit FP operations Intel did not widen the available 128-bit data paths to
256 bits but made use of both the 128-bit FX and FP data paths available on the same port.
4.2.2 Extension of the ISA by the AVX instruction set (8)
For example, a 256-bit multiply instruction can be issued to port 0 and simultaneously use
the 128-bit SIMD data path for the low half and the 128-bit FP data path for the high half
of the operands.
This implementation needs some extra logic, but it saves substantial silicon area and power.
We note that the two AVX execution units are 256-bit wide but they do not yet support FMA
instructions.

## Slide 177
Intel redesigned large parts of the microarchitecture of the cores, as indicated by yellow boxes
in the Figure below.
Figure 4.2.2.1: Microarchitecture of the cores of Sandy Bridge [64]
Implementation of AVX -2
4.2.2 Extension of the ISA by the AVX instruction set (9)

## Slide 178
4.2.3 New microarchitectures of the cores (1)
4.2.3 New microarchitecture of the cores
Intel redesigned large parts of the microarchitecture of the cores, as indicated by yellow boxes
in the Figure below.
Figure 4.2.3.1: Microarchitecture of the cores of Sandy Bridge [64]

## Slide 179: 4.2.3 New microarchitectures of the cores (2)
The micro-op cache [213]
It can hold 3.5 K micro-operations (micro-ops).
Assuming an average x86 instruction length of 3.5 byte the micro-op cache is equivalent to
an instruction cache of about 5.2 kB.
The micro-op cache replaces Nehalem's loop-buffer that also stores micro-ops, nevertheless
only up to 28 items.
The micro-op cache holds already decoded instructions, thus instructions whose micro-ops
are already available in the micro-op cache do not need to be fetched, predecoded,
decoded and converted to micro-ops a new.
Here we assume that the micro-op cache has its own branch unit to follow instruction traces.
According to Intel, the hit rate of the micro-op cache is about 80 %.
This raises performance and reduces power consumption.
I

## Slide 180: 4.2.3 New microarchitectures of the cores (3)
Remark
The micro-op cache is similar to Intel's Trache Cache
introduced in their pentium 4 family in 2000.
Figure: Trace Cache of the Pentium 4 [214]

## Slide 181
Here we do not want to go into details of the microarchitecture, but refer to two very detailed
descriptions [64], [98].
4.2.3 New microarchitectures of the cores (4)

## Slide 182: 4.2.4 On-die ring interconnect bus (1)
4.2.4 On die ring interconnect bus [66]
The ring has six bus stops for
interconnecting
The four cores and the
L3 slices share the same
interfaces.
four cores
four L3 slices
the GPU and
the System Agent
System Agent

## Slide 183: 4.2.4 On-die ring interconnect bus (2)
Main feature of the on-die interconnect bus [64]
• It operates at core frequency (One stop/clock)

## Slide 184: 4.2.5 On die graphics unit (1)
Evolution of graphics implementation from Westmere to Sandy Bridge [99]
4.2.5 On die graphics unit [99]

## Slide 185: 4.2.5 On die graphics unit (2)
Support of both media and graphics processing by the graphics unit [99]

## Slide 186: 4.2.5 On die graphics unit (3)
Main features of the on die graphics unit [99]
12 EUs
8.2.5 On die graphics unit (1)

## Slide 187: 4.2.5 On die graphics unit (4)
Specification data of the HD 2000 and HD 3000 graphics [100]
-
8.2.5 On die graphics unit (1)

## Slide 188: 4.2.5 On die graphics unit (5)
Execution units (EU) of the graphics unit in Sandy Bridge [197]
Each EU is basically a 4-wide SP FP SIMD unit intended to operate on 4-component data
(RGBA), capable of executing 2-operation MAD instructions and also FX instructions.
EUs are 5-way multithreaded for GT2 graphics and 4-way multithreaded for GT1 graphics.
Each thread has a register set of 120 32 B registers.
There is also a fixed function Math Box for executing transcendental, e.g. trigonometric
instructions and also FP divide.
The EUs do not support DP FP operations.
Figure: Block diagram of an EU of the graphics unit of Sandy Bridge
RGBA: RGB Alpha (opacity)

## Slide 189: 4.2.5 On die graphics unit (9)
frames per sec
i5/i7 2xxx/3xxx:
Sandy Bridge
i5 6xx
Arrandale
HD 5570
400 ALUs
Performance comparison of the Sandy Bridge’s graphics: gaming [101]

## Slide 190: 4.2.6 Turbo Boost technology 2.0 (1)
Cooler
Designated also as the 2.0 generation Turbo Boost technology.
Thermal capacitance
The concept utilizes the real temperature response of processors to power changes
in order to increase the extent of overclocking [64].
4.2.6 Turbo Boost 2.0 technology [64]

## Slide 191: 4.2.6 Turbo Boost technology 2.0 (2)
Main aspects of Intel’s Turbo Boost Technology 2.0 [198]

## Slide 192
Based on the real temperature response the thermal energy budget accumulated during idle
periods can be utilized to push the core beyond the TDP for short periods of time (e.g. for 20 sec).
Multiple algorithms manage in parallel current, power and die temperature. [64]
4.2.6 Boost technology 2.0 (3)

## Slide 193
Intelligent power sharing between the cores and the integrated graphics [64]
4.2.6 Enhanced Turbo Boost technology (4)
Figure: Power sharing between CPU and GPU [207]

## Slide 194
[61]
WSM/M
WSM/D
NHM/M
NHM/D
4.2.6 Enhanced Turbo Boost technology (5)

## Slide 195
Remark
Individual cores may run at different frequencies but all cores share the same power plane.
Individual cores may be shut down if idle by power gates.
4.2.6 Enhanced Turbo Boost technology (6)

## Slide 196
4.3 Example for a Sandy Bridge based desktop
platform with the H67 chipset
Notes: 196

## Slide 197: 4.3 Example for a Sandy Bridge based desktop platform with the H67 chipset (1)
4.3 Example for a Sandy Bridge based desktop platform with the H67 chipset [102]

## Slide 198
5. The Haswell line
5.1 Introduction
5.2 Major enhancements of the Haswell line vs.
the Sandy Bridge line
5.3 Major innovations of the Haswell line
5.4 Haswell based mobile and desktop processors
Notes: 198

## Slide 199
5.1 Introduction
Notes: 199

## Slide 200: 5.1 Introduction (1)
Launched: 6/2013 at Computex.
5.1 Introduction
Haswell processors are termed also as the 4. gen. Intel Core processors, as indicated below.
Figure : Intel’s Tick-Tock development model (Based on [1])
Figure 4.1.1: Intel’s Tick-Tock development model (Based on [1])
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
1. gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
Skylake
New
Microarchi.
14 nm
TOCK
6. gen.

## Slide 201: 1. Introduction (12)
Figure : Overview of Intel’s Tick-Tock model (Based on [3])
New microarch.,
64-bit
New microarch.: 4-wide core,
128-bit SIMD FX/FP EUs,
shared L2 , no HT
11/2007
01/2006
90nm
130nm
TICK TOCK
2 YEARS
2 YEARS
2 YEARS
65nm
TICK Pentium 4 / Cedar Mill
TOCK Core 2
2 YEARS
New microarch.
New microarch.,
hyperthreading (HT)
Pentium 4 /Northwood
TICK TOCK
TICK TOCK
Pentium 4 /Prescott
Pentium 4 /Willamette
07/2006
11/2008
New microarch.: 256-bit (FP) AVX,
ring bus, integr. GPU
11/2000
01/2002
02/2004
Key new features of the ISP
and the microarchitecture
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
180nm
256-bit( FX) AVX2,
L4 cache (discrete eDRAM), FIVR
06/2013
09/2014
Shared Virtual Memory
08/2015
ISP,
Memory Side $ (eDRAM), No FIVR
In package integr. GPU
14nm
2 YEARS
TICK Broadwell
TOCK Skylake
New microarch.: integrated MC, QPI,
(inclusive) L3, HT
The Haswell line

## Slide 202: 5.1 Introduction (3)
DP/MP servers (Haswell-EP, Haswell-EX)
They were launched later, in 09/2014 and 05/2014, as indicated subsequently.
A second wave of Haswell processors, called the Haswell refresh processors launched in
5/2014.
They do not provide any significant changes vs. the first released processors.
Actually, the manufacturing process could be made more efficient and this resulted in slight
improvements in clock speeds.
The Haswell refresh processors [176]
The Haswell line
Launched in 06/2013
22 nm IC technology

## Slide 203: 5.1 Introduction (4)
Desktops (2-chip designs)
Overview of the Haswell family-1
Core i7-49xx/48xx/472x/471x/470x, 4C+G, HT, 6/2013 and 5/2014
Core i7-46xx/45xx, 2C+G, HT, 5/2013 and 6/2014
Core i5-43xx/42xx U/Y, 2C+G, HT, 6/2013 and 5/2014
Core i3-41xx/40xx, 2C+G, HT, 6/2013 and 5/2014
Core i7-479x/478x/477x,476x, 4C+G, HT, 6/2013 and 5/2014
Core i5-46xx/45xx/44xx, 4C+G, HT, 6/2013 and 5/2014
Core i3-43xx/41xx, 2C+G, HT, 6/2013, 5/2014 and 3/2015
i7-5960X/5930K/5820K, 6/8 C, 8/2014
Servers
(See on a subsequent slide)
Haswell
(LGA1150)
Up to 4 cores
(This Section)
Haswell-E
(LGA2011)
Up to 8 cores
(Not discussed here)
The Haswell family
Haswell-EP
(LGA2011)
Up to 18 cores
(Not discussed ere)
Haswell-EX
(LG2011)
Up to 18 cores
(Not discussed here)
Mobiles (SoCs)
Notes: ridge-ex

## Slide 204: 5.1 Introduction (5)
M – mobile processor (Socket G3
Q – quad-core
U – ultra-low power (BGA 1168 packaging)
X – "extreme"
Y – extreme low-power (BGA 1168 packaging)
E / H – BGA 1364 packaging
K – unlocked (adjustable CPU multiplier up to 63x)
S – performance-optimized lifestyle (low power with 65 W TDP)
T – power-optimized lifestyle (ultra low power with 35–45 W TDP)
R – BGA packaging / High-performance GPU (currently Iris Pro 5200 (GT3e))
X – extreme performance (adjustable CPU ratio with no ratio limit)
Interpretation of the mobile suffixes
Interpretation of the desktop suffixes
Interpretation of the model suffixes of the mobile and desktop lines [205]
BGA packaging (Ball Grid Array): for soldering
LGA packaging (Land Grid Array): removable

## Slide 205: 5.1 Introduction (6)
Haswell
(LGA1150)
Up to 4 cores
(This Section)
Haswell-E
(LGA2011)
Up to 8 cores
(Not discussed here)
The Haswell family
Haswell-EP
(LGA2011)
Up to 18 cores
(Not discussed here)
Haswell-EX
(LG2011)
Up to 18 cores
(Not discussed here)
Servers
Microservers
E3-1275L/1265L v3, 4C+G, HT, 6/2013 and 5/2014
E3-1240L/1230L/1220L v3, 2C/4C, HT, 6/2013 and 5/2014
UP Servers
E3-12x5/12x6 v3, 4C+G, HT, 6/2013 and 5/2014
E3-12x0/12x1 v3, 4C, HT, 6/2013 and 5/2014
E5-16xx v3, 4/6/8, 9/2014
Workstations
DP-Servers
MP-Servers
E5-26xx v3, 4/6/8/10/12/14/16/18C, 9/2014
E5-46xx v3, 6/10/12/14/16/18C, 6/2015
E7-48xx v3, 8/10/12/14, 5/2015
E7-88xx v3, 4/10/16/18C, 5/2015
Overview of the Haswell family-2

## Slide 206: 5.1 Introduction (7)
Note
Mobiles, desktops, microservers and UP servers include two or four cores,
high-end desktops (E-series) 6 to 8 cores whereas
workstations, DP and MP servers typically more, up to 18 cores,
as indicated in the above overviews.

## Slide 207: 5.1 Introduction (7)
Die plot of a quad core Haswell processor [121]

## Slide 208: 5.1 Introduction (9)
Die plot of a dual core Haswell processor [177]

## Slide 209: 5.1 Introduction (10)
In package integrated CPU and PCH for mobile processors [204]
BGA: Ball Grid Array
PGA: Pin Grid array

## Slide 210: 5.1 Introduction (11)
Single thread IPC in Intel’s basic architectures [195]
20%
18%
16%
14%
12%
10%
8%
6%
4%
2%
0%
1.8
1.7
1.6
1.5
1.4
1.3
1.1
1.2
1
Per Generation
Cumulative
Pentium M
Dothan
Core 2
Penryn
NHM (w/o SMT)
WSM
SNB
IVB
HSW
BRW

## Slide 211
5.2 Major enhancements of the Haswell line vs.
the Sandy Bridge line
5.2.1 Overview
5.2.3 Enhanced microarchitecture for the cores
5.2.4 Enhanced graphics
5.2.2 ISA extension (of the cores) by the AVX2
instruction set
Notes: 211

## Slide 212: 5.2.1 Overview (1)
5.2 Major enhanchements of the Haswell line vs. the Sandy Bridge line
5.2.1 Overview
ISA extension by the AVX2
instruction set (Section 5.2.2)
Enhanced microarchitecture for the cores
(Section 5.2.3)
Enhanced graphics (Section 5.2.4)

## Slide 213: 5.2.2 ISA extension by the AVX2 instruction set (1)
5.2.2 ISA extension by the AVX2 instruction set -1 [97]
FMA: Fused Multiply-Add

## Slide 214: 5.2.2 ISA extension by the AVX2 instruction set (2)
ISA extension by the AVX2 instruction set -2 [80]

## Slide 215: 5.2.2 ISA extension by the AVX2 instruction set (3)
Example for calculating D = A x B + C with 8 32-bit data vectors by using the AVX2
ISA extension [212]

## Slide 216: 5.2.2 ISA extension by the AVX2 instruction set (4)
When the processor detects AVX instructions it signals it to the PCU (Power Control Unit).
Then the PCU delivers higher core voltage that however increases the dissipation.
At the same time while executing AVX instructions the PCU reduces the clock frequency
of the processor. to remain within the TDP limit and avoid overheating.
The higher voltage will remain for 1 ms after the last AVX instruction completes and
, subsequently the core voltage will return to its nominal value defined by the TDP.
Remark
Reduced core frequency while running AVX instructions
AVX base: it is the minimum frequency for workloíds using AVX instructions.
AVX max all core Turbo: it is the maximum frequency for workloads using all cores
for executing AVX instructions.
Figure: Core frequency limits in Haswell-EP and
previous lines [212]
Related to this, Intel added two AVX frequencies for their Haswell- EP (E5-1600 and E5-2600
line of processors, as follows and demonstrated in an example.
(128-bit execution)

## Slide 217: 5.2.2 ISA extension by the AVX2 instruction set (5)
AVX Frequency Range Example – E5-2699 v3
Example: Core frequency limits for Intel's E5-2699 v3 processor [212]

## Slide 218: 5.2.2 ISA extension by the AVX2 instruction set (6)
Evolution of the AVX ISA extensions [97]

## Slide 219: 5.2.2 ISA extension by the AVX2 instruction set (7)
Expected future evolution of AVX [165]

## Slide 220: 5.2.3 Enhanced microarchitecture for the cores (1)
5.2.3 Enhanced microarchitecture for the cores [80]

## Slide 221: 5.2.3 Enhanced microarchitecture for the cores (2)
Buffer sizes of subsequent generations of the Core processors [80]

## Slide 222: 5.2.3 Enhanced microarchitecture for the cores (3)
Cache sizes, latencies and bandwidth values of subsequent Core generations [122]

## Slide 223: 5.2.3 Enhanced microarchitecture for the cores (4)
Issue rate and execution unit enhancements of Haswell [165]
FMA: Fused Multiply-Add (a x b+c)

## Slide 224
5.2.4 Enhanced graphics (1)
5.2.4 Enhanced graphics
To compete with AMD’s advanced graphics solutions Intel put a great emphasis on enhancing
Haswell’s integrated graphics.
Sliced graphics architecture to allow scaling of EUs
Inclusion of eDRAM in high-end units.
Main features of the new graphics units: are termed as Iris Pro and Iris graphics.

## Slide 225: 5.2.4 Enhanced graphics (2)
a) Introduction of sliced graphics architecture
The new graphics architecture of Haswell is sliced, to allow scaling of EUs by using one or two slices/unit.
Each slice has two sub-slices, with up to 10 EUs/sub-slice, as indicated in the Figure below.
Figure: A sub-slice with 10 EUs
of the graphics unit of Haswell [199]

## Slide 226: 5.2.4 Enhanced graphics (3)
A slice of the graphics unit of Haswell including two sub-slices with 20 EUs [199]

## Slide 227: 5.2.4 Enhanced graphics (4)
The architecture of a GT3 graphics unit of Haswell including two slices with 40 EUs [199]

## Slide 228: 5.2.4 Enhanced graphics (5)
Block diagram of an EU of Haswell -1 [199]
Each EU has four functional units:
Two 4-way SIMD FPU units
1 Send unit (Load/Store) and
1 Branch unit.
An EU issues up to 4 instructions per cycle to the functional units.

## Slide 229: 5.2.4 Enhanced graphics (6)
Block diagram of an EU of Haswell -2 [199]
Each SIMD FPUs can execute 4 SP FP or 1/2/4/8/16/32 bit wide FX operations.
They can execute MAD instructions (Multiply-Add) per cycle.
Thus an EU can execute 2 FPU x SIMD4 x 2 (MAD) = 16 SP FP operations/cycle.
The EU is 7-way multithreaded.
Each thread has 128 32 B registers.
One of the FPUs also supports FX operations.
One of the FPUs also support transcendental math functions.

## Slide 230: 5.2.4 Enhanced graphics (7)
Interpretation of the notions Graphics Technology (GT) for the Haswell line and
subsequent lines
GT1 designates graphics with a single slice and reduces execution resources (less sub-slices
or less EUs per sub-slice)
GT2 designates graphics with a single slice (e.g. 20 EUs in the Haswell line)
GT3 designates graphics with dual slices (e.g. 40 EUs in the Haswell line)
GT4 designates graphics with triple slices.

## Slide 231: 5.2.4 Enhanced graphics (8)
Introducing the notions Iris/Iris Pro graphics
Intel designates their
high-end graphics as Iris graphics and
high-end graphics enhanced with embedded DRAM (eDRAM) as Iris Pro graphics.
The inclusion of eDRAM will be indicated also in the GT naming by supplementing the GT level
by the letter “e”, so GT3e designates GT3 level with eDRAM.
Iris graphics unit
Iris Pro graphics unit
Haswell’s Iris graphics unit
(They incorporate two slices with altogether 40 EUs
It is enhanced by a 128 MB sized
on package integrated eDRAM
It is not enhanced by an
on package integrated eDRAM

## Slide 232: 5.2.4 Enhanced graphics (9)
b)Inclusion of eDRAM in high-end graphics units
It will be discussed in Section 5.3.1

## Slide 233: 5.2.4 Enhanced graphics (10)
Intel Core generation | Graphics generation | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Westmere | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 7th | HD 2500 | GT1 | 1 (6 EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 8th | HD 5300- HD 5600 | GT2 | 1(3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  | HD 535 | GT3 | 2 | 48 |  |  |  | 
 |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Evolution of main features of Intel’s graphics families

## Slide 234: 5.2.4 Enhanced graphics (11)
Haswell
Sandy Bridge
Ivy Bridge
Graphics performance increase of subsequent Core generations [117]

## Slide 235
5.3 Major innovations of the Haswell line
5.3.1 On-package eDRAM cache
5.3.2 FIVR (Fully Integrated Voltage Regulator)
5.3.3 TSX (Transactional Synchronization Extensions)
Notes: 235

## Slide 236: 5.3 Major innovations of the Haswell line (1)
5.3 Major innovations of the Haswell line
On-package e-DRAM cache (Section 5.3.1)
FIVR (Fully Integrated Voltage Regulator) (Section 5.3.2)
TSX (Transactional Synchronization Extensions) (Section 5.3)

## Slide 237: 5.3.1 On-package eDRAM cache (1)
5.3.1 On-package eDRAM cache [117]

## Slide 238: 5.3.1 On-package eDRAM cache (2)
Principle of operation [117]
The on package eDRAM, designated also as Crystallwell, it operates as a true 4th level cache
of the memory hierarchy.
It acts as a victim buffer to the L3 cache, in the sense that anything evicted from the
L3 cache immediately goes into the L4 cache.
Both CPU and GPU requests are cached.
The cache partitioning between CPU and GPU is dynamic.
If the GPU is not in use the whole L4 cache may be devoted the CPU, in this case the CPU
has a 128 MB L4 cache.
Access latency after an L3 miss is 30 – 32 ns.
The L4 cache is capable of delivering 50 GB/s in each direction.
The Crystallwell die consumes between 0.5 and 1.0 W if idle and between 3.5 and 4.5 W
under full load.
The PCU (Power Control Unit) of the processor takes over the power management of the
eDRAM, beyond the power management of the CPU cores, GPU, L3 cache etc.

## Slide 239: 5.3.1 On-package eDRAM cache (3)
Implemented on-package eDRAM [124]
eDRAM chip

## Slide 240: 5.3.1 On-package eDRAM cache (4)
L1
L2
L3
L4
Memory
Memory latency vs. access range in a memory system with eDRAM cache (L4) [117]
Ivy Bridge
Ivy Haswel with Chrystallwelll
Ivy Haswell without CRW

## Slide 241: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (1)
Before introducing FIVR into the Haswell family, motherboards for Intel processors had to provide
6 different voltage regulators (VRs) to supply different voltages to the CPU cores, graphics (Gfx),
System Agent (SA), IO, PLL and Memory, as indicated in the next Figure.
5.3.2 FIVR (Fully Integrated Voltage Regulator) -1
Figure: Voltage Regulators (VRs) needed in motherboards of Intel processors before introducing
FIVRs [178]

## Slide 242: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (2)
FIVR integrates legacy power delivery onto the package and the die, as shown below for
intel's Haswell processor[178]
Figure: Integrating legacy power delivery onto the package and the die with FIVR [178]
This consolidates five platform VRs into one and thus greatly simplifies mainboard design.
FIVR (Fully Integrated Voltage Regulator) -2

## Slide 243: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (3)
Contrasting power delivery in Ivy Bridge and Haswell platforms [149]

## Slide 244: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (4)
Implementation of the voltage planes in desktop and mobile Haswell processors [173]

## Slide 245: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (5)
Functional partitioning of Haswell’s FIVR implementation [150]
Functional partitioning
The first stage of the voltage regulator converts
from the PSU or battery voltage (12V)
to approximately 1.8V, which is distributed
across the microprocessor die.
The second conversion stage is comprised of
between 8 and 31 (depending on the
product) FIVRs, which are 140MHz
synchronous multiphase buck converters
with up to 16 phases.
FIVR is built up of two stages.
12 V
First stage
Second stage

## Slide 246: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (6)
Partitioning of the implementation [150]
The first stage is on the
motherboard.
The inductors and the midfrequency decoupling capacitors are placed on the package.
The power FETs, control circuitry and high frequency decoupling are on the die.
Each FIVR is independently programmable to achieve optimal operation given the requirements of the domain it is powering.
The settings are optimized by the Power Control Unit (PCU), which specifies the input voltage, output voltage, number of operating phases, and a variety of other settings to minimize the total power consumption of the die.

## Slide 247: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (7)
Figure: Block diagram of the Buck converter [151]
Principle of operation of the Buck converter [151]
On state
Off state
Figure: Operation of the Buck converter [151]
Q: MOSFET
Drive circuit:
E.g. PWM modulated
(Pulse Width Modulated)

## Slide 248: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (8)
Fig. 9: Principle of a synchronous n-phase buck converter [152]
Enhancing the buck converter to synchronous n-phase buck design to reduce ripple [152]

## Slide 249: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (9)
Simplified block diagram of a single voltage plane in the FIVR domain of Haswell [150]
VID: Parallel Voltage Identification code

## Slide 250: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (10)
Board space saving with Haswell’s FIVR vs. Ivy Bridge’s voltage regulator [149]

## Slide 251: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (11)
FIVR and per-core P-state control
FIVR obviously provides an appropriate technique to deliver per-core core voltages and thus
its use can greatly simplify the implementation of per-core P-state control.
Despite this fact only the server and workstation oriented Haswell-EP lines (including the
Xeon E5-1600 v3, the Xeon E5 2600 v3 and Xeon E5-4600 v3 processor lines) make use
of this feature, as seen in the next slide for the Xeon E5-2600 v3, whereas mobile,
desktop or Haswell-E oriented lines do not.
By contrast, all cores on Ivy Bridge and previous generations, run at the same frequency
and are supplied by the same voltage.
We note that per-core P-state needs additional BIOS and OS support for scheduling the
cores.
Moreover, according to available documentation the high-end Haswell-EX server line do not
implement FIVR at all presumable due to heat problems.

## Slide 252: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (12)
Per Core P-State (PCPS) management in Intel’s E5-2600 v3 (Haswell-EP) [172]

## Slide 253: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (13)
Assessment of FIVR - its benefits [178]

## Slide 254: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (14)
FIVR clearly increases the power dissipation of the processor package and thus it has a
limiting effect on the TDP and consequently on the performance.
Assessment of FIVR - its drawbacks [178]

## Slide 255: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (15)
In their subsequent Broadwell family (9/2014) Intel introduced the 2nd generation FIVR with 3DL
design [155]
3DL: 3D Layering
PCB: Printed Circuit Board
Caps: Capacitors
LVR: Linear Voltage Generator
Remark
of about 30 % []
http://hothardware.com/reviews/intel-core-m-broadwell-architecture-preview?page=3

## Slide 256: 5.3.2 FIVR (Fully Integrated Voltage Regulator) (16)
Due to its drawbacks, after using FIVR in Broadwell, Intel decided to remove it in their upcoming Skylake and Kaby Lake processors.
Accordingly, related motherboards need again to provide appropriate power delivery.
Nevertheless, sources state that in the subsequent 10 nm Cannonlake processors, due to
in 2017, Intel will anew make use of the FIVR technology probably as future FIVR designs
will achieve higher efficiency and thus generate less heat [211].
The future of FIVR

## Slide 257: 5.3.3 TSX (Transactional Synchronization Extensions)
5.3.3 TSX (Transactional Synchronization Extensions)
Haswell also introduced a further new feature, called the Transactional Synchronization Extensions
(TSX) that was debuted on selected Haswell models (SKUs)..
TSX supports Transactional Memory in hardware (to be discussed later in the Chapter
high end MP servers).
Nevertheless, in August 2014 Intel announced a bug in the TSX implementation on all current
steppings of all Haswell models an disabled the TSX feature on affected CPUs via a microcode
update.
Subsequently, TSX became enabled first on a Broadwell model (Core M-5Y70) in 11/2014
then on the Haswell-EX in 5/2015.
SKU: Stock Keeping Unit

## Slide 258
5.4 Haswell based mobile and desktop processors
Notes: 258

## Slide 259: 5.4 Haswell based mobile and desktop processors (1)
Desktops (2 chips)
Servers
5.4 Haswell based mobile and desktop processors
Core i7-49xx/48xx/472x/471x/470x, 4C+G, HT, 6/2013 and 5/2014
Core i7-46xx/45xx, 2C+G, HT, 5/2013 and 6/2014
Core i5-43xx/42xx U/Y, 2C+G, HT, 6/2013 and 5/2014
Core i3-41xx/40xx, 2C+G, HT, 6/2013 and 5/2014
Core i7-479x/478x/477x,476x, 4C+G, HT, 6/2013 and 5/2014
Core i5-46xx/45xx/44xx, 4C+G, HT, 6/2013 and 5/2014
Core i3-43xx/41xx, 2C+G, HT, 6/2013, 5/2014 and 3/2015
i7-5960X/5930K/5820K, 6/8 C, 8/2014
(See next slide)
Haswell
(LGA 1150)
Up to 4 cores
(This Section)
Haswell-E
(LGA 2011)
Up to 8 cores
(Not discussed here)
The Haswell family
Haswell-EP
(LGA 2011)
Up to 18 cores
(Not discussed ere)
Haswell-EX
(LGA 2011)
Up to 18 cores
(Not discussed here)
Mobiles (SoCs)
Notes: ridge-ex

## Slide 260
Intel 4th Gen Core i7 M-Series Mobile Processors |  |  |  |  | 
Model | Core i7-4930MX | Core i7-4900MQ | Core i7-4800MQ | Core i7-4702MQ | Core i7-4700MQ
Cores/Threads | 4/8 | 4/8 | 4/8 | 4/8 | 4/8
CPU Base Freq | 3.0 | 2.8 | 2.7 | 2.2 | 2.4
Max SC Turbo | 3.9 | 3.8 | 3.7 | 3.2 | 3.4
Max DC Turbo | 3.8 | 3.7 | 3.6 | 3.1 | 3.3
Max QC Turbo | 3.7 | 3.6 | 3.5 | 2.9 | 3.2
TDP | 57W | 47W | 47W | 37W | 47W
HD Graphics | 4600 | 4600 | 4600 | 4600 | 4600
GPU Clock | 400-1350 | 400-1300 | 400-1300 | 400-1150 | 400-1150
L3 Cache | 8MB | 8MB | 6MB | 6MB | 6MB
DDR3/DDR3L | 1600 | 1600 | 1600 | 1600 | 1600
vPro/TXT/VT-d | Yes | Yes | Yes | No | No
Intel SBA | No | No | No | Yes | Yes
Price | $1096 | $568 | $378 |  | 
Main features of first introduced Haswell-based mobile Core i7 M-Series processors [125]
5.4 Haswell based mobile and desktop processors (2)

## Slide 261
Intel 4th Gen Core i7 Desktop Processors |  |  |  |  |  | 
Model | Core i7-4770K | Core i7-4770 | Core i7-4770S | Core i7-4770T | Core i7-4770R | Core i7-4765T
Cores/Threads | 4/8 | 4/8 | 4/8 | 4/8 | 4/8 | 4/8
CPU Base Freq | 3.5 | 3.4 | 3.1 | 2.5 | 3.2 | 2.0
Max Turbo | 3.9 (Unlocked) | 3.9 | 3.9 | 3.7 | 3.9 | 3.0
Test TDP | 84W | 84W | 65W | 45W | 65W | 35W
HD Graphics | 4600 | 4600 | 4600 | 4600 | Iris Pro 5200 | 4600
GPU Max Clock | 1250 | 1200 | 1200 | 1200 | 1300 | 1200
L3 Cache | 8MB | 8MB | 8MB | 8MB | 6MB | 8MB
DDR3 Support | 1333/1600 | 1333/1600 | 1333/1600 | 1333/1600 | 1333/1600 | 1333/1600
vPro/TXT/VT-d/SIPP | No | Yes | Yes | Yes | No | Yes
Package | LGA-1150 | LGA-1150 | LGA-1150 | LGA-1150 | BGA | LGA-1150
Price | $339 | $303 | $303 | $303 |  | $303
Main features of first issued Haswell-based Core i7 desktop processors [126]
5.4 Haswell based mobile and desktop processors (3)

## Slide 262
Example of a Haswell-based desktop platform [145]
5.4 Haswell based mobile and desktop processors (4)

## Slide 263
Integer and FP performance of subsequent generations of desktop processors [127]
Sandy Bridge
Ivy Bridge
Haswell
5.4 Haswell based mobile and desktop processors (5)

## Slide 264
Note
As the AVX2 extension of the Haswell processors introduces 256-bit FX operations, this line
has a considerable higher integer performance than previous Core generations.
5.4 Haswell based mobile and desktop processors (6)

## Slide 265
Graphics performance of subsequent generations of desktop processors [127]
Sandy Bridge
Ivy Bridge
Haswell
5.4 Haswell based mobile and desktop processors (7)

## Slide 266
6. The Skylake line
6.1 Introduction
6.2 Major enhancements of the Skylake line vs.
the Broadwell line
6.3 Major innovations of the Skylake line
6.4 Skylake based processor lines
Notes: 266

## Slide 267
6.1 Introduction
Notes: 267

## Slide 268: 6.1 Introduction (1)
5.1 Introduction (1)
6.1 Introduction
Skylake processors are termed also as the 6. gen. Intel Core processors, as indicated below.
Figure : Intel’s Tick-Tock development model (Based on [1])
Core 2
New
Microarch.
65 nm
Penryn
New
Process
45 nm
Nehalem
New
Microarch.
45 nm
West-
mere
New
Process
32 nm
Sandy Bridge
New
Microarch.
32 nm
Ivy Bridge
New
Process
22 nm
Haswell
New
Microarchi.
22 nm
TOCK
TICK
TOCK
TICK
TOCK
TICK
TOCK
1. gen.
2. gen.
3. gen.
4. gen.
5. gen.
Broad-
well
New
Process
14 nm
TICK
Skylake
New
Microarchi.
14 nm
TOCK
6. gen.
The Skylake line is built on 14 nm technology.
Launched: 08/2015

## Slide 269: 1. Introduction (12)
Figure : Overview of Intel’s Tick-Tock model (Based on [3])
New microarch.,
64-bit
New microarch.: 4-wide core,
128-bit SIMD FX/FP EUs,
shared L2 , no HT
11/2007
01/2006
90nm
130nm
TICK TOCK
2 YEARS
2 YEARS
2 YEARS
65nm
TICK Pentium 4 / Cedar Mill
TOCK Core 2
2 YEARS
New microarch.
New microarch.,
hyperthreading (HT)
Pentium 4 /Northwood
TICK TOCK
TICK TOCK
Pentium 4 /Prescott
Pentium 4 /Willamette
07/2006
11/2008
New microarch.: 256-bit (FP) AVX,
ring bus, integr. GPU
11/2000
01/2002
02/2004
Key new features of the ISP
and the microarchitecture
01/2011
01/2010
32nm
45nm
2 YEARS
2 YEARS
22nm
2 YEARS
TICK Penryn Family
TOCK Nehalem
TICK Westmere
TOCK Sandy Bridge
TICK Ivy Bridge
TOCK Haswell
04/2012
180nm
256-bit( FX) AVX2,
L4 cache (discrete eDRAM), FIVR
06/2013
09/2014
Shared Virtual Memory
08/2015
ISP,
Memory Side $ (eDRAM), No FIVR
In package integr. GPU
14nm
2 YEARS
TICK Broadwell
TOCK Skylake
New microarch.: integrated MC, QPI,
(inclusive) L3, HT
The Skylake line

## Slide 270: 6.1 Introduction (3)
According to sources quoting Intel’s statements [206] on average, Skylake has 10% better
performance, 30% better graphics performance.
Performance improvements provided by Skylake

## Slide 271: 6.1 Introduction (4)
Per Generation
Cumulative
Pentium M Dothan
Core 2
Penryn
NHM (w/o SMT)
WSM
SNB
IVB
HSW
BRW
1.8
1.7
1.6
1.5
1.4
1.3
1.1
1.2
1
2
1.9
20%
18%
16%
14%
12%
10%
8%
6%
4%
2%
0%
24%
22%
SKL
Single thread IPC in Intel’s basic architectures (Based on [195])
Note that Intel raised IPC in the Core family only less then 2-times in about 10 years.

## Slide 272: 6.1 Introduction (5)
4.5 W
15/28 W
45 W
65/91 W
Skylake Series -1 [206]

## Slide 273: 6.1 Introduction (6)
Skylake Series -2 [202]
BGA: Ball Grid Array (to be soldered)
LGA: Land Grid Array (to be socketed)

## Slide 274: 6.1 Introduction (7)
This diagram shows a kind of "superset" of Skylake. Different versions will not include all
of these parts, but these are all the different components that can be included.
Main enhancements and innovations of Intel’s Skylake microarchitecture [200]

## Slide 275: 6.1 Introduction (8)
The Skylake die [208]

## Slide 276
6.2 Major enhancements of the Skylake line
6.2.1 More advanced microarchitecture of the cores
6.2.2 Enhanced graphics
Notes: 276

## Slide 277: 6.2 Major enhancements of the Skylake line
6.2 Major enhancements of the Skylake line
6.2.1 More advanced microarchitecture of the cores

## Slide 278: 6.2.1 More advanced microarchitecture of the cores (1)
Instruction window (ROB), buffer and register sizes of subsequent generations of the
Core 2 family [200]

## Slide 279: 6.2.2 Enhanced graphics (1)
Skylake
Broadwell
Haswell
Ivy Bridge
Sandy Bridge
6.2.2 Enhanced graphics
Performance increase of Intel’s graphics over generations [196]

## Slide 280: 6.2.2 Enhanced graphics (2)
Intel Core generation | Graphics generation | Models | Graphics Technology level | No. of graphics slices | No. of EUs | eDRAM | OpenGL version | DirectX version | OpenCL version
Westmere | 5th (Ironlake) | HD |  |  | 12 | -- | 2.1 | 10.1 | n.a.
Sandy Bridge | 6th | HD 2000 | GT1 | 1 (2x3 EU) | 6 |  | 3.1/3.3 | 10.1 | n.a.
 |  | HD 3000 | GT2 | 1 (4x3 EU) | 12 |  |  |  | 
Ivy Bridge | 7th | HD 2500 | GT1 | 1 (6 EU) | 6 | -- | 4.0 | 11.0 | 1.2
 |  | HD 4000 | GT2 | 1 (2x8 EU) | 16 |  |  |  | 
Haswell | 7.5th | HD 4200- HD 4700 | GT2 | 1 (2x10 EU) | 20 | -- | 4.3 | 11.1 | 1.2
 |  | HD 5000 Iris 5100 | GT3 | 2 | 40 |  |  |  | 
 |  | Iris Pro 5200 |  |  |  | 128 MB |  |  | 
Broadwell | 8th | HD 5300- HD 5600 | GT2 | 1 (3x8 EU) | 23/24 | -- | 4.3 | 11.2 | 2.0
 |  | HD 6000 Iris 6100 | GT3 | 2 | 47/48 |  |  |  | 
 |  | Iris Pro 6200 | GT3e | 2 | 48 | 128 MB |  |  | 
Skylake | 9th | HD 510 | GT1 | 1 (3x4 EU) | 12 | -- | 4.4 | 12 | 2.0
 |  | HD 515 | GT1.5 | 1 (3x6 EU) | 18 |  |  |  | 
 |  | HD 520 | GT2 | 1 (3x8 EU) | 24 |  |  |  | 
 |  | HD 530 | GT2 | 1 | 24 |  |  |  | 
 |  | HD 540 | GT3e | 2 | 48 | 64 MB |  |  | 
 |  | HD 580 | GT4e | 3 | 72 | 64/128 MB |  |  | 
Evolution of main features of Intel’s graphics families

## Slide 281: 6.2.2 Enhanced graphics (3)
Expected main features of the Skylake line [190]

## Slide 282: 6.2.2 Enhanced graphics (4)
Skylake/Gen9 graphics architecture overview [196]
GT2

## Slide 283: 6.2.2 Enhanced graphics (5)
Gen9 graphics scalability -1 [196]

## Slide 284: 6.2.2 Enhanced graphics (6)
Gen9 graphics scalability -2 [196]

## Slide 285: 6.2.2 Enhanced graphics (7)
Scaling for GT 1.5 to reduce power
Gen9 graphics scalability -3 [196]

## Slide 286: 6.2.2 Enhanced graphics (8)
Gen9 graphics Codec support [196], [201]
With the new hardware accelerated codec solution watching a movie or video conferencing
can be done by highly efficient fixed-function circuits rather than by using more flexible, but
more power hungry CPU and GPU cores [201]

## Slide 287: 6.2.2 Enhanced graphics (9)
Gen9 graphics display support [201]
It supports 3 display pipes.
WiDi is Intel’s Wireless Display technology to transmit music, videos, movies, photos etc.
from a WiDi compatible computer to a compatible HDTV.
The initial version of WiDi supported only a low resolution of 720p, Skylake provides already
HD quality with a resolution of 1080.
Miracast is a WiDi standard of the Wi-Fi Alliance providing HD quality.

## Slide 288: 6.2.2 Enhanced graphics (10)
Note
Skylake does not make use of the FIVR technology, as indicated in the Figure below.
The reason for omitting FIVR in Skylake (and probably also is the subsequent Cannonlake) is
that it increases unduly the die temperature and limits overclocking.
Figure: Voltage domains of Skylake [200]
Note that all cores share the same voltage
and even the same frequency.

## Slide 289
6.3 Major innovations of the Skylake line
6.3.1 Integrated ISP (Image Signal Processing)
6.3.2 Memory Side Cache
6.3.3 Innovations in power management
Notes: 289

## Slide 290: 6.3.1 Integrated ISP (Image Signal Processing) (1)
6.3 Major innovations of the Skylake line
6.3.1 Integrated ISP (Image Signal Processing) [200]
BOM: Bill of Material

## Slide 291: 6.3.2 Memory Side Cache (MSC) (1)
The eDRAM cache of Broadwell [200]
6.3.2 Memory Side Cache (MSC)
Note: The L4 eDRAM cache operates as a victim cache to the L3 (LLC).

## Slide 292: 6.3.2 Memory Side Cache (MSC) (2)
MS$: Memory Side Cache
Memory Side Cache of the Skylake [200]
CTL: Control

## Slide 293: 6.3.2 Memory Side Cache (MSC) (3)
Benefits of the Memory Side Cache (MSC) [200]
It is fully coherent.
Available for use by I/O devices and the Display engine as well.

## Slide 294: 6.3.3 Innovations in power management
6.3.3 Innovations in power management
6.3.3.1 SpeedShift Technology
6.3.3.2 Duty cycle control of the cores

## Slide 295: 6.3.3.1 Speed Shift Technology (1)
6.3.3.1 Speed Shift Technology [198]
The legacy power management technology, called the DVFS (Dynamic Voltage and
Frequency Scaling) -1
Intel’s DVFS implementation is called the Enhanced SpeedStep Technology (EIST), introduced along with the Pentium M processor (~2003).
It is based on the the ACPI interface specification that is an interface between the OS and the computer system aiming at supporting power management.
DVFS is demand based, meaning that the OS determines the actual level how far the actual
workload utilizes a core and selects the appropriate working point, called P point, for the
core.
Each Pi point represents the operating {fci, Vci} values as seen in the figure below.
Example: Intel’s Enhanced SpeedStep technology introduced in the Pentium M (~2003) [210]
P1
P2
P6

## Slide 296: 6.3.3.1 Speed Shift Technology (2)
In given intervalls of about 10 ms the OS calculates the workload demand for a core
by dividing the number of clock cycles used by the number of all clock cycles.
While taking into account both the user specified power management policy that
reflects the user’s power management priority (such as max. performance, longest
battery life or balanced) and the workload demand, the OS selects the appropriate
P point (the needed fc and the associated Vci) for the core.
The selected fci/Vci value will be communicated to the processor by writing these values
into a defined register set (actually three processor registers rpresenting a register
interface between the OS and the processor) that is specified by the ACPI standard.
Finally, the processor uses these values to set the PLL and the voltage regulator accordingly.
Principle of operation of DVFS -2
Figure: Example for how EIST operates while ramping up performance [218]
fc in GHz
ms

## Slide 297: 6.3.3.1 Speed Shift Technology (3)
Principle of operation of DVFS -2
Note that a requested ramping up the performance will be performed in a series of smaller
steps to maintain data integrity.

## Slide 298: 6.3.3.1 Speed Shift Technology (4)
Extension of DVFS by Turbo Boost technolgy and Thermal control
On the other hand, when the workload demands a higher
operating point than P1, the processor can take over the
control over the power management by activating the
turbo boost technology.
Lower than Pn states (called t-states (Throttling states))
are used typically for thermal control to manage critical
thermal conditions, like overheating the die.
Note
Each DVFS implementation, such as Intel's EIST or AMD's PowerNow' needs appropriate
OS support, typically provided beginning with a specified OS version.

## Slide 299: 6.3.3.1 Speed Shift Technology (5)
The drawback of DVFS implemented by the Enhanced SpeedStep technology
One of the basic drawback of the enhanced SpeedStep technology is slow responsiveness,
e.g. 30 ms responsiveness, needed until the OS recognizes the change of operating
conditions (typically workload demand) and the processor responds by modifying the
operating point [201].
This is unfavorable for low residency workloads, like quickly changing video recording.

## Slide 300: 6.3.3.1 Speed Shift Technology (6)
The Speed Shift Technology -1
It is called also as the Hardware Controlled Performance States (HWP).
It is an implementation of the Collaborative Processor Performance Control (CPPC) feature
introduced in the ACPI version 5.0.
As long as the Enhanced SpeedStep technology makes use of P-states and the OS
communicates the performance demand of the workload to the processor by writing the
requested P-state (fc, Vc values) into a given processor register, the Speed Shift Technology
specifies the workload directed performance demand as an abstract performance level
that is not directly tied to the P-states and writes it into a different processor register,
defined in the ACPI version 5.
Based on the specified performance level written into the given processor register, the PCU
(Power Control Unit) of the processor selects the appropriate fc and Vcc values for running
the workload.
This is a finer grained control mechanism than the P-state based one (as indicated in the
next slide) since the PCU can now select any feasible clock frequency (clock frequencies
are the product of the bus frequency (133 MHz) and an integer clock multiplier
(e.g. 20 for 2.667 GHz) within a highest and lowest clock frequency whereas P-states are
typically coarser grained.

## Slide 301: 6.3.3.1 Speed Shift Technology (7)
Contrasting the P-state based EIST power management with the Speed Shift
technology [218]

## Slide 302: 6.3.3.1 Speed Shift Technology (8)
The OS can even transfer frequency control partially or fully to the PCU of theprocessor,
as the next Figures show.
The Speed Shift Technology -2

## Slide 303: 6.3.3.1 Speed Shift Technology (9)
Passing power management control for all P-states to the CPU [198]

## Slide 304: 6.3.3.1 Speed Shift Technology (10)
Passing power management control for a subset of P-states to the CPU [198]

## Slide 305: 6.3.3.1 Speed Shift Technology (11)
When the OS specifies the requested performance level and transfers subsequently
the power management control to the PCU the following benefit arises:
In many cases performance needs to be raised quickly (e.g. to support performance
bursts by web browsing or office work).
But Vc can not be ramped up in a single step instead only in a few smaller steps to
preserve data integrity.
If the performance control is performed by the OS, the OS needs multiple steps, each
lasting about 10 to 20 ms.
By contrast, if the control is transferred to the PCU, the PCU is capable to fulfil
each step in 1 or a few ms.
Consequently, while using the Speed Shift technology performance bursts may be
performed much faster and this may result in higher performance, as the next
Figure indicates.
The Speed Shift Technology -3

## Slide 306: 6.3.3.1 Speed Shift Technology (12)
Benefit of the Speed Shift technology: faster ramping up performance if needed [218]
fc [GHz]
ms

## Slide 307: 6.3.3.1 Speed Shift Technology (13)
The Speed Shift technology was the result of a cooperation between Intel and Microsoft.
It needs Windows 10 with an appropriate extension and recently runs only on Skylake models.
The Speed Shift Technology -4

## Slide 308: 6.3.3.1 Speed Shift Technology (14)
Contrasting the performance scores while runnung the WebXPRT 2015 benchmark
[228]
Principled Technologies's WebXPRT runs a series of tests to measure browser's performance,
i.e. HTML and Javascript handling, as well as tasks like photo manipulation and face detection
[219].
We note that the above speed up result is more or less exceptional, in most published
benchmarks Intel's Speed Shift technology provides only a few percent imrovement
in performance or power consumption, as indicated e.g. in the next Figure.

## Slide 309: 6.3.3.1 Speed Shift Technology (15)
Contrasting the performance scores while runnung the PCMark 8 - Home benchmark
[228]

## Slide 310: 6.3.3.2 Duty cycle control (1)
While running applications
dynamic dissipation: ~ f3
runtime: ~ 1/f
total energy consumption originating from the dynamic dissipation: ~ f2
with f denoting the clock frequency.
As the performance ~ f, the energy consumption originating from the dynamic dissipation
depends on the performance as shown below.
Figure: Dependence of energy consumption originating from the dynamic dissipation
(designated as Compute energy in the Figure) on the performance (~ f) [198]
6.3.3.2 Duty cycle control [198]

## Slide 311: 6.3.3.2 Duty cycle control (2)
On the other hand
the total energy consumption originating from static dissipation and system power depends
on the runtime, i.e.
the total energy consumption originating from static dissipation and system power: 1/f,
as indicated in the Figure below.
Figure: Dependence of energy consumption originating from the static dissipation
and system power (designated as SoC and system energy in the Figure) on the performance (~ f) [198]

## Slide 312: 6.3.3.2 Duty cycle control (3)
As a consequence, the total energy consumption originating from both the
dynamic dissipation and
static dissipation as well as system power consumption
has a minimum, as indicated in the Figure below.
Figure: Dependence of energy consumption originating from both the dynamic dissipation (designated as the Compute energy in the Figure) and the static dissipation and system power (designated as SoC and system energy in the Figure) on the performance
Obviously, the min. energy consumption point (Pe) is the most efficient working point of a core
of the processor.

## Slide 313: 6.3.3.2 Duty cycle control (4)
Power management with taking into account the most efficient Pe working point [198]
Frequency will be lowered as far as possible until the Pe working point is reached.
Pe will be calculated every ms based on the workload and system characteristics.
There is no benefit when the system is clocked below the Pe point, as it would increase
the energy consumption.
Therefore, a so called EARtH algoritm overrides lower P requests and sets f according to Pe.
The EARtH algorithm is activated only if it is possible to enter the package sleep state.
Figure: Power management with taking into account the most efficient Pe working point [198]

## Slide 314: 6.3.3.2 Duty cycle control (5)
Duty cycling [198]
While managing power going below Pe would reduce energy consumption inefficiently
due to the fixed power components.
In this region turning the package on and off, called duty cycling, reduces power
proportionally to run time, as shown in the Figure below.
Duty cycling is more effective technique to reduce power for low computing demand in the
region below Pe than reducing frequency below the value associated with Pe..
Figure: Principle of duty cycling used to reduce energy consumption in the region below Pe

## Slide 315
6.4 The Skylake-based processor lines
Notes: 315

## Slide 316: 6.4 The Skylake-based processor lines (1)
Key features of the Skylake lines -1 [202]
Dies: No. of cores and GT levels, e.g. 2+2 means: 2 cores +GT 2 graphics, etc.
6.4 The Skylake based processor lines

## Slide 317: 6.4 The Skylake-based processor lines (2)
Key features of the Skylake line -2 [190]

## Slide 318: 6.4 The Skylake-based processor lines (3)
Expected launch dates of the Skylakes Series [192]

## Slide 319: 6.4 The Skylake-based processor lines (4)
Mobiles (SoC designs)
4.5 W Core M-line (Y-line) (BGA1515)
Core m7-6Y7x, 2C+HD 515, HT, 9/2015
1. Introduction (2)
The Skylake (6th Gen) mobile and desktop lines - Overview
Core m5-6Y5x, 2C+HD 515, HT, 9/2015
Core m3-6Y3x, 2C+HD 515, HT, 9/2015
Core i7-66x0U/65x0U, 2C+HD 515, HT, 9/2015
Core i5-63x0U/62x0U, 2C+HD 515, HT, 9/2015
Core i3-6100U, 2C+HD 515, HT, 9/2015
15 W U-line (BGA1356)
Core i7-65x7U, 2C+HD 550, HT, 9/2015
Core i5-62x7U, 2C+HD 550, HT, 9/2015
Core i3-61x7U, 2C+HD 550, HT, 9/2015
28 W U-line (SoC, BGA1356)

## Slide 320: 6.4 The Skylake-based processor lines (5)
Desktops (2-chip designs, 100 Series chipset)
Core i7-6700T 4C+HD 530, HT, 9/2015
Core i5-6600T/6500T/6400T, 4C+HD 530, HT, 9/2015
Core i3-6300T/6100T, 2C+HD 530, HT, 9/2015
35 W S-lines (LGA 1151)
Core i7-6700K/6600K, 4C, HT, 8/2015
91 W S-lines, unlocked (LGA1151)
Microservers
45 W v5-lines (BGA)
Xeon E3-15x5M v5, 4C+HD 530, HT, 9/2015
Core i7-6920HQ/6820HQ/6700HQ, 4C+HD 530, HT, 9/2015
Core i5-6440HQ/6300HQ, 4C+HD 530, HT, 9/2015
Core i3-6100H, 2C+HD 530, HT, 9/2015
45 W HQ/H-lines (BGA1440)
Core i7-6700, 4C+HD 530, HT, 9/2015
Core i5-6600/6500/6400 4C+HD 530, HT, 9/2015
Core i3-6320/6300/6100, 2C+HD 530, HT, 9/2015
65 W S-lines (LGA 1151)

## Slide 321: 6.4 The Skylake-based processor lines (6)
Example 1: Main features of the models of the 4.5 W Skylake m-line [202]

## Slide 322: 6.4 The Skylake-based processor lines (7)
Example 2: Main features of the models of the 91 W unlocked Skylake S-line [202]
Note that the 91 W unlocked Skylake S-line does not include integrated graphics, as most users
of this high-end processor will attach discrete graphics cards.

## Slide 323: 6.4 The Skylake-based processor lines (8)
TDP (W) | No. of cores | Graphics | No. of graphics EUs | eDRAM | Base frequency (GHz)
4.5 | 2 | HD 515 | 18 | -- | 1.2
15 | 2 | HD 540 | 48 | 64 MB | 2.2
15 | 2 | HD 520 | 24 | -- | 2.6
28 | 2 | HD 550 | 48 | 64 MB | 3.3
35 | 4 | HD 530 | 24 | -- | 2.8
45 | 4 | HD 530 | 24 | -- | 2.9
65 | 4 | HD 530 | 24 | -- | 3.4
91 | 4 | -- | -- | -- | 4.2
The max. base frequency of Skylake models with different TDPs and configurations
(Based on data from [202])
Note that low TDP can be achieved first of all by reducing the core frequency and limiting
the computer resources (cores, GPU EUs) provided.

## Slide 324: 6.4 The Skylake-based processor lines (9)
Intel Core i7-6700K desktop processor platform [203]

## Slide 325
7. The Kaby Lake line
Notes: 325

## Slide 326: 7. The Kaby Lake line (1)
Preliminary information about the Kaby Lake line [179]
It is actually a Skylake refresh line (actually a TIck line) manufactured on 14 nm technology.
Its aim is to stretch out the lifespan of the 14 nm process technology.
Desktop chips will use the the same socket type (LGA1151) as the preceeding Skylake chips.
Announced on Intel’s Q2 2015 conference call.
Launched: in 08/2016, it will be followed by the 10 nm Cannonlake in 2H 2017.
This means that the cadence of Intel’s technology transitions slowed down to about 2.5 years,
as Kranich, Intel’s CEO formulated:
The last two technology transitions have signaled that our cadence today is closer to
2.5 years than two."

## Slide 327: 7. The Kaby Lake line (2)
IMAGE
Variant | KBL-Y (BGA) | KBL-U (BGA) | KBL-H (BGA) | KBL-S (LGA) | KBL-S (LGA)
Cores Configurations | 2 | 2/2 | 4/4 | 2/4/4 | 4/4
Graphic Configurations | GT2 | GT2/GT3 | GT2/GT4 | GT2/GT2/GT4 | GT0/GT2
eDRAM | N/A | N/A / 64 MB | N/A / 256 MB | N/A / N/A/ 64 MB | N/A
SOC Design | Yes | Yes | No External PCH | No External PCH | No External PCH
TDP | 4.5W | 15W / 28W | 35W / 45W / TBD | 35W / 65W / 91W | 25W / 45W / 80W
Expected main features of the Kaby Lake line [194]

## Slide 328: 7. The Kaby Lake line (3)
Expected system architecture of a U or Y-Series Kaby Lake processor [194]

## Slide 329
8. References
Notes: 329

## Slide 330: References (1)
[1]: Singhal R., “Next Generation Intel Microarchitecture (Nehalem) Family: Architecture Insight
and Power Management, IDF Taipeh, Oct. 2008, http://intel.wingateweb.com/taiwan08/
published/sessions/TPTS001/FA08%20IDFTaipei_TPTS001_100.pdf
[2]: Bryant D., “Intel Hitting on All Cylinders,” UBS Conf., Nov. 2007,
http://files.shareholder.com/downloads/INTC/0x0x191011/e2b3bcc5-0a37-4d06-
aa5a-0c46e8a1a76d/UBSConfNov2007Bryant.pdf
[3]: Fisher S., “Technical Overview of the 45 nm Next Generation Intel Core Microarchitecture
(Penryn),” IDF 2007, ITPS001, http://isdlibrary.intel-dispatch.com/isd/89/45nm.pdf
[4]: De Gelas J., “Intel Core versus AMD’s K8 architecture,” AnandTech, May 1 2006,
http://www.anandtech.com/cpuchipsets/intel/showdoc.aspx?i=2748&p=1
[5]: Carmean D., “Inside the Pentium 4 Processor Micro-architecture,” Aug. 2000,
http://people.virginia.edu/~zl4j/CS854/pda_s01_cd.pdf
[6]: Shimpi A. L. & Clark J., “AMD Opteron 248 vs. Intel Xeon 2.8: 2-way Web Servers
go Head to Head,” AnandTech, Dec. 17 2003,
http://www.anandtech.com/showdoc.aspx?i=1935&p=1
[7]: Völkel F., “Duel of the Titans: Opteron vs. Xeon : Hammer Time: AMD On The Attack,”
Tom’s hardware, Apr. 22 2003,
http://www.tomshardware.com/reviews/duel-titans,620.html
[8]: De Gelas J., “Intel Woodcrest, AMD's Opteron and Sun's UltraSparc T1:
Server CPU Shoot-out,” AnandTech, June 17 2006,
http://www.anandtech.com/IT/showdoc.aspx?i=2772&p=1

## Slide 331: References (2)
[10]: Wechsler O., “Inside Intel Core Microarchitecture,” White Paper, Intel, 2006
[11]: Lee V., “Inside the Intel Core Microarchitecture,” IDF, May 2006, Shenzhen,
http://www.prcidf.com.cn/sz/systems_conf/track_sz/SMC/Intel%20Core%20uArch.pdf
[12]: Doweck J., “Inside Intel Core Microarchitecture,” Hot Chips 18, 2006,
http://www.hotchips.org/archives/hc18/
[13]: Gruen H., “Intel’s new Core Microarchitecture,” Develop Brighton, AMD Technical
Day, July 2006,
http://ati.amd.com/developer/brighton/03%20Intel%20MicroArchitecture.pdf
[14]: Doweck J., “Intel Smart Memory access: Minimizing Latency on Intel Core
Microarchitecture, ” Technology @ intel Magazine, Sept. 2006, pp. 1-7,
ftp://download.intel.com/corporate/pressroom/emea/deu/fotos/06-10-Strategie_Tag/
Intel/Intel_Core2_Prozessoren/Texte/ENG-Smart_Memory_Access_Technology@
Intel_Magazine_Article.pdf
[15]: Sima D., Fountain T., Kacsuk P., Advanced Computer Architectures, Addison Wesley,
Harlow etc., 1997
[16]: Jafarjead B., “Intel Core Duo Processor,” Intel, 2006,
http://masih0111.persiangig.com/document/peresentation/behrooz%20jafarnejad.ppt
[17]: Pawlowski S. & Wechsler O., “Intel Core Microarchitecture,” IDF Spring, 2006,
http://www.intel.com/pressroom/kits/core2duo/pdf/ICM_tech_overview.pdf
[9]: Hinton G. & al., “The Microarchitecture of the Pentium 4 Processor,” Intel Technology
Journal, Q1 2001, pp. 1-13

## Slide 332: References (3)
[21]: Kim N. S. et al., „Leakage Current: Moore’s Law Meets Static Power”, Computer,
Dec. 2003, pp. 68-75.
[22]: Ng P. K., “High End Desktop Platform Design Overview for the Next Generation
Intel Microarchitecture (Nehalem) Processor,” IDF Taipei, TDPS001, 2008,
http://intel.wingateweb.com/taiwan08/published/sessions/TDPS001/
FA08%20IDF-Taipei_TDPS001_100.pdf
[23]: Bohr M., Mistry K., Smith S., “Intel Demonstrates High-k + Metal Gate Transistor
Breakthrough in 45 nm Microprocessors,”, Intel, Jan. 2007,
http://download.intel.com/pressroom/kits/45nm/Press45nm107_FINAL.pdf
[24]: Scott D. S., “Toward Petascale and Beyond,” APAC Conference, Oct. 2007,
http://www.apac.edu.au/apac07/pages/program/presentations/
Tuesday%20Harbour%20A%20B/David_Scott.pdf
[25]: Smith S. L., “45 nm Product Press Briefing,” IDF Fall, 2007,
http://download.intel.com/pressroom/kits/events/idffall_2007/BriefingSmith45nm.pdf
[26]: Fisher S., “Technical Overview of the 45nm Next Generation Intel Core Microarchitecture
(Penryn),” IPTS001, Fall IDF 2007, http://isdlibrary.intel-dispatch.com/isd/89/45nm.pdf
[19]: SIMD Instruction Sets, http://softpixel.com/~cwright/programming/simd/index.php
[20]: Wikipedia: Platform Environment Control Interface,
http://en.wikipedia.org/wiki/Platform_Environment_Control_Interface
[18]: Goto H., Larrrabee architecture can be integrated into CPU”, PC Watch, Oct. 6 2008,
http://pc.watch.impress.co.jp/docs/2008/1006/kaigai470.htm

## Slide 333: References (4)
[31]: Gelsinger P. P., “Intel Architecture, Press Briefing, March 2008,
http://www.slideshare.net/angsikod/gelsinger-briefing-on-intel-architecture
[32]: Gelsinger P., “Invent the new reality,” IDF Fall 2008, San Francisco
http://download.intel.com/pressroom/kits/events/idffall_2008/PatGelsinger_day1.pdf
[33]: Brayton J.,”Nehalem: Talk of the Tock, Intel Next Generation Microprocessor,” IDF,
April 2008, Shanghai,
http://inteldeveloperforum.com.edgesuite.net/shanghai_2008/ti/TCH001/f.htm
[34]: Intel Timna Microprocessor Family, CPU World, http://www.cpu-world.com/CPUs/Timna/
[35]: Smith T., “Timna - Intel's first system-on-a-chip, Before 'Tolapai', before 'Banias'.
Register Hardware, Febr. 6 2007,
http://www.reghardware.co.uk/2007/02/06/forgotten_tech_intel_timna/
[28]: Wikipedia: Foxton Technology, http://en.wikipedia.org/wiki/Foxton_Technology
[29]: Coke J. & al., “Improvements in the Intel Core Penryn Processor Family Architecture
and Microarchitecture,” Intel Technology Journal, Vol. 12, No. 3, 2008, pp. 179-192
[30]: Fisher S., “Technical Overview of the 45nm Next Generation Intel Core Microarchitecture
(Penryn),” BMA S004, IDF 2007,
http://my.ocworkbench.com/bbs/attachment.php?attachmentid=318&d=1176911500
[27]: George V., 45nm Next Generation Intel Core Microarchitecture (Penryn),” Hot Chips 19,
2007, http://www.hotchips.org/archives/hc19/3_Tues/HC19.08/HC19.08.01.pdf

## Slide 334: References (5)
[38]: Strong B., “A Look Inside Intel: The Core (Nehalem) Microarchitecture,”
http://www.cs.utexas.edu/users/cart/arch/beeman.ppt
[39]: Valles A. C., Ansari Z., Mehrotra P.: “Tuning Your Software for the Next Generation
Intel Microarchitecture (Nehalem) Family,” IDF 2008, NGMS002,
http://www.benchmark.rs/tests/editorial/Nehalem_munich/presentations/
Software-Tuning_for_Nehalem.pdf
[40]: The low cost Tymna CPU, Tom’s hardware, Febr. 25 2000,
http://www.tomshardware.com/reviews/idf-2000,166-3.html
[41]: Intel® Virtualization Technology, Special issue, Vol. 10 No. 03 Aug. 2006, http://www.intel.com/technology/itj/2006/v10i3/
[37]: Singhal R. Intel’s i7, Podtech, http://www.podtech.net/home/5436/intels-core-i7
[36]: Images, Xtreview,
http://xtreview.com/images/K10%20processor%2045nm%20architec%203.jpg
[42]: Intel Core 2 Duo Processor E8000 and E7000 Series Datasheet, Intel, Jan. 2009
[43]: Wikipedia: List of Intel Core 2 microprocessors
http://en.wikipedia.org/wiki/List_of_Intel_Core_2_microprocessors
[44]: Wikipedia: Nehalem (microarchitecture)
http://en.wikipedia.org/wiki/Nehalem_(microarchitecture)
[45]: Glaskowsky P.: Investigating Intel's Lynnfield mysteries, cnet News, Sept. 21 2009,
http://news.cnet.com/8301-13512_3-10357328-23.html

## Slide 335: References (6)
[48]: Intel CoreTM i7-800 and i5-700 Desktop Processor Series Datasheet – Volume 1,
July 2010, http://download.intel.com/design/processor/datashts/322164.pdf
[50]: Intel CoreTM i7-900 Mobile Processor Extreme Edition Series, Intel Core i7-800 and
i7-700 Mobile Processor Series, Datasheet – Volume One, Sept. 2009
http://download.intel.com/design/processor/datashts/320765.pdf
[51]: Intel Turbo Boost Technology in Intel CoreTM Microarchitecture (Nehalem) Based
Processors, White Paper, Nov. 2008 http://download.intel.com/design/processor/applnots/320354.pdf
[47]: Intel Xeon Processor C5500/C3500 Series, Datasheet – Volume 1, Febr. 2010,
http://download.intel.com/embedded/processor/datasheet/323103.pdf
[46]: Shimpi A. L.: Intel's Core i7 870 & i5 750, Lynnfield: Harder, Better, Faster Stronger,
AnandTech, Sept. 8 2009, http://www.anandtech.com/show/2832
[52]: Power Management in Intel Architecture Servers, White Paper, April 2009
http://download.intel.com/support/motherboards/server/sb/power_management_
of_intel_architecture_servers.pdf
[53]: Glaskowsky P.: Explaining Intel’s Turbo Boost technology, cnet News, Sept. 28 2009,
http://news.cnet.com/8301-13512_3-10362882-23.html
[49]: Glaskowsky P.: Intel's Lynnfield mysteries solved, cnet News, Sept. 28 2009,
http://news.cnet.com/8301-13512_3-10362512-23.html
[54]: Intel Xeon Processor 7500 Series, Datasheet – Volume 2, March 2010
http://www.intel.com/Assets/PDF/datasheet/323341.pdf

## Slide 336: References (7)
[58]: Hill D., Chowdhury M.: Westmere Xeon-56xx „Tick” CPU, Hot Chips 2010
http://www.hotchips.org/uploads/archive22/HC22.24.620-Hill-Intel-WSM-EP-print.pdf
[59]: Intel CoreTM i7-600, i5-500, i5-400 and i3-300 Mobile Processor Series, Datasheet -
Vol.1, Jan. 2010, http://download.intel.com/design/processor/datashts/322812.pdf
[56]: Kottapalli S., Baxter J.: Nehalem-EX CPU Architecture, Hot Chips 2009, Sept. 10 2009
http://www.hotchips.org/archives/hc21/2_mon/HC21.24.100.ServerSystemsI-Epub/
HC21.24.122-Kottapalli-Intel-NHM-EX.pdf
[55]: Pawlowski S.: Intelligent and Expandable High- End Intel Server Platform, Codenamed
Nehalem-EX, IDF 2009
[60]: Nagaraj D., Kottapalli S.: Westmere-EX: A 20 thread server CPU, Hot Chips 2010
http://www.hotchips.org/uploads/archive22/HC22.24.610-Nagara-Intel-6-Westmere-EX.pdf
[57]: Kurd N. A. & all: A Family of 32 nm IA Processors, IEEE Journal of Solide-State Circuits,
Vol. 46, Issue 1., Jan. 2011, pp. 119-130
[61]: Kahn O., Piazza T., Valentine B.: Technology Insight: Intel Next Generation
Microarchitecture Codename Sandy Bridge, IDF 2010
extreme.pcgameshardware.de/.../281270d1288260884-bonusmaterial-pc- games-
hardware-12-2010-sf10_spcs001_100.pdf
[62]: Wikipedia: Sandy Bridge, http://en.wikipedia.org/wiki/Sandy_Bridge
[63]: http://ark.intel.com
[64]: Kahn O., Valentine B.: Intel Next Generation Microarchitecture Codename Sandy Bridge:
New Processor Innovations, IDF 2010

## Slide 337: References (8)
[65]: Shimpi A. L.: Intel Pentium 4 1.4GHz & 1.5GHz, AnandTech, Nov. 20 2000
http://www.anandtech.com/show/661/5
[66]: Yuffe M., Knoll E., Mehalel M., Shor J., Kurts T.: A fully integrated multi-CPU, GPU and
memory controller 32nm processor, ISSCC, Febr. 20-24 2011, pp. 264-266
[67]: Intel Xeon Processor 7500/6500 Series, Public Gold Presentation, Data Center Group,
March 30. 2010, http://cache-www.intel.com/cd/00/00/44/64/446456_446456.pdf
[68]: Tang H., Cheng H.: Intel Xeon Processor E3 Family Based Servers: A Smart Investment
for Managing Your Small Business, IDF 2011
[69]: Thomadakis M. E. PhD: The Architecture of the Nehalem Processor and Nehalem-EP SMP
Platforms, Texas A&M University, March 17 2011
http://alphamike.tamu.edu/web_home/papers/perf_nehalem.pdf
[70]: Intel Xeon Processor E7-8800/4800/2800 Product Families, Datasheet Vol. 1 of 2,
April 2011, http://www.intel.com/Assets/PDF/datasheet/325119.pdf
[71]: Mitchell D., Intel Nehalem-EX review, PCPro,
http://www.pcpro.co.uk/reviews/processors/357709/intel-nehalem-ex
[72]: Rusu & al.: A 45 nm 8-Core Enterprise Xeon Processor, IEEE journal of Solid State Circuits,
Vol. 45, No. 1, Jan. 2010, pp. 7-14
[73]: Wechsler O., Multicore Archtecture Challenges and Opportunities, Intel’s Annual Symposium
on VLSI CAD and Validation, Keynote presentation, July 2007
http://www3.ee.technion.ac.il/sites/Workshop/upload/Events/ACRC%20-%20Intel/
Ofri-Wechsler%20Keynotes%20Speech.pdf

## Slide 338
References (9)
[74]: Razin A., Core, Nehalem, Gesher. Intel: New Architecture Every Two Years,
Xbit Laboratories, April 28 2006,
http://www.xbitlabs.com/news/cpu/display/20060428162855.html
[75]: Har_Even B., Justin Rattner Keynote? Trusted Reviews, April 17 2007,
http://www.trustedreviews.com/news/IDF-Spring-2007-Day-One-Opening-Keynote
[76]: Weatherstone R., Intel Core i7-3960X Extreme Edition Processor (Sandy Bridge-E)
Review, Nov. 14 2011, Vortez, http://www.vortez.net/articles_pages/intel_core_i7_
3960x_extreme_edition_processor_sandy_bridge_e,2.html
[77]: Shimpi A. L., Intel Core i7 3960X (Sandy Bridge E) Review: Keeping the High End Alive,
Nov. 14 2011, AnandTech, http://www.anandtech.com/show/5091/intel-core-i7-3960x-
sandy-bridge-e-review-keeping-the-high-end-alive/4
[78]: Intel® X79 Express Chipset, http://www.intel.com/content/www/us/en/chipsets/
performance-chipsets/x79-express-chipset.html
[79]: Intel® Desktop Board DX79SI Extreme Series, 2011, http://www.intel.com/content/
dam/doc/product-brief/desktop-board-dx79si-extreme-brief.pdf
[81]: Olivera, A régóta várt Intel Ivy Bridge tesztje, Prohardware, April 13 2012,
http://prohardver.hu/teszt/intel_ivy_bridge_teszt/az_ivy_bridge.html
[80]: Chappell R., Toll B., Singhal R.: Intel Next Generation Microarchitecture Codename Haswell:
New Processor Innovations, IDF 2012

## Slide 339
[82]: Bohr M., Mistry K.: Intel’s Revolutionary 22 nm transistor technology, May 2011,
http://download.intel.com/newsroom/kits/22nm/pdfs/22nm-Details_Presentation.pdf
[83]: George V., Piazza T., Jiang H.: Technology Insight: Intel Next Generation Microarchitecture
Codename Ivy Bridge, IDF 2011
[84]: 3rd Generation Intel Core Processor Family Quad Core Launch Product Information,
April 23 2012, http://download.intel.com/newsroom/kits/core/3rdgen/pdfs/3rd_Generation
_Intel_Core_Product_Information.pdf
[85]: Ivy Bridge and Haswell die configurations (estimates included), Anandtech, March 21 2012,
http://forums.anandtech.com/showthread.php?t=2234017
[86]: Piazza T., Jiang H., Hammerlund P., Singhal R.: Technology Insight: Intel Next Generation
Microarchitecture Codename Haswell, IDF 2012 SPCS001
[87]: Haynes D.: 2012 Socket Guide, Aug. 4 2012,
http://www.ocmodshop.com/cpu-socket-guide-2012/lga2011/
[88]: O’Shea P., Thermal management solutions include support for Intel platform environmental
control interface, EE Times, Oct. 17 2006,
http://www.eetimes.com/document.asp?doc_id=1301982
[90]: Shimpi A. L., The Intel Core i3 530 Review - Great for Overclockers & Gamers,
AnandTech, Jan. 22 2010, http://www.anandtech.com/show/2921
[89]: Altavilla D., Intel Arrandale Core i5 and Core i3 Mobile Unveiled, Hot Hardware, Jan. 4 2010,
http://hothardware.com/Reviews/Intel-Arrandale-Core-i5-and-Core-i3-Mobile-Unveiled/
References (10)

## Slide 340
[91]: Chiappetta M., Intel Clarkdale Core i5 Desktop Processor Debuts, Hot Hardware, Jan. 3 2010,
http://hothardware.com/Articles/Intel-Clarkdale-Core-i5-Desktop-Processor-Debuts/
[92]: Thomas S. L., Desktop Platform Design Overview for Intel Microarchitecture (Nehalem)
Based Platform, Presentation ARCS001, IDF 2009
[93]: Kirsch N., Intel Core i7-980X Six-Core Processor Extreme Edition Review, Legit Reviews,
March 11 2010, http://www.legitreviews.com/intel-core-i7-980x-six-core-processor-
extreme-edition-review_1245
[94]: Kanter D., Westmere Arrives, Real World Tech, March 17 2010,
http://www.realworldtech.com/westmere/2/
[95]: Hruska J., Intel Unveils 10-Core Xeons, Mission-Critical Servers, Hot Hardware, Apr. 5 2011,
http://hothardware.com/Reviews/Intel-Unveils-10Core-Xeons-MissionCritical-Servers/
[96]: Intel Sandy Bridge Review, Bit-tech, Jan. 3 2011,
http://www.bit-tech.net/hardware/cpus/2011/01/03/intel-sandy-bridge-review/1
[97]: Toll B., Locktyukhin M., Girkar M., Intel Advanced Vector Extensions 2 and Bit Manipulation
New Instructions, IDF 2012
[99]: Piazza T., Dr. Jiang H., Microarchitecture Codename Sandy Bridge: Processor
Graphics, Presentation ARCS002, IDF San Francisco, Sept. 2010
[98]: Torres G., Inside the Intel Sandy Bridge Microarchitecture, Hardware Secrets, Dec. 30 2010,
http://www.hardwaresecrets.com/article/Inside-the-Intel-Sandy-Bridge-Microarchitecture/1161/2
References (11)

## Slide 341
[100]: Wikipedia: Intel GMA, 2011, http://en.wikipedia.org/wiki/Intel_GMA
[101]: Shimpi A. L., The Sandy Bridge Review: Intel Core i7-2600K, i5-2500K and Core i3-2100
Tested, AnandTech, Jan. 3 2011, http://www.anandtech.com/show/4083/the-sandy-
bridge-review-intel-core-i7-600k-i5-2500k-core-i3-2100-tested/11
[102]: Intel® Q67 Express Chipset, http://www.intel.com/content/www/us/en/chipsets/
mainstream-chipsets/q67-express-chipset.html
[103]: Rodolf K., Small and Medium Business Server Solutions from Intel, Sept. 20 2012
[104]: Intel Core i7 Processor Family for the LGA-2011 Socket, Datasheet, Vol.1, Nov. 2012,
http://www.intel.com/content/www/us/en/processors/core/core-i7-lga-2011-datasheet-
vol-1.html
[105]: Crijns K., nVidia GeForce GTX 680 Quad-SLI review, Hardware.info, March 23 2012,
http://nl.hardware.info/reviews/2641/nvidia-geforce-gtx-680-quad-sli-review-english-version
[106]: Wikipedia: List of Intel Xeon microprocessors,
http://en.wikipedia.org/wiki/List_of_Intel_Xeon_microprocessors#Sandy_Bridge-based_Xeons
[108]: Intel Xeon E5-2690 001, CPU, Tom’s Hardware, http://www.tomshardware.com/gallery/
Intel-Xeon-E5-2690-001,0101-320460-0-2-3-1-jpg-.html
[107]: Morgan T.P., Intel plugs both your sockets with 'Jaketown' Xeon E5-2600s, The Register,
March 6 2012, http://www.theregister.co.uk/2012/03/06/intel_xeon_2600_server_
chip_launch/
References (12)

## Slide 342
[109]: System Architecture and Configuration, Oct. 2012,
http://www.qdpma.com/systemarchitecture/SystemArchitecture_2012Q4.html
[110]: Intel Xeon Processor E5-1600/E5-2600/E5-4600 Product Families, Datasheet, Vol.1,
May 2012, http://www.intel.la/content/www/xl/es/processors/xeon/xeon-e5-1600-2600-
vol-1-datasheet.html
[111]: Bolaria J., Romley Revamps Server Platforms, The Linley Group, April 2 2012,
http://www.linleygroup.com/mpr/article.php?id=10879
[112]: Angelini C., Intel Xeon E5-2600: Doing Damage With Two Eight-Core CPUs, Tom’s Hardware,
March 6 2012, http://www.tomshardware.com/reviews/xeon-e5-2687w-benchmark-
review,3149-10.html
[113]: Ulvr P., Fait F., Built to Scale: Introducing the Intel Xeon Processor E5 Family, 2012,
http://www-05.ibm.com/cz/events/truck2012/bp/pdf/system_x_cast/Intel_Xeon_E5_
obchodni.pdf
[114]: Panagiotidis N.G., Intel Xeon: the Enabling Technology to the Performing, Flexible & Energy
efficient Cloud Infrastructure, April 23 2013,
http://www.cisco.com/web/GR/connect2013/pdfs/007_intel_nikos_panagiotidis.pdf
[116]: Vilches J., Intel Ivy Bridge: everything you need to know, TechSpot, March 8 2012,
http://www.techspot.com/guides/502-intel-ivy-bridge/page3.html
[115]: Wikipedia: Ivy Bridge (microarchitecture),
http://en.wikipedia.org/wiki/Ivy_Bridge_%28microarchitecture%29
References (13)

## Slide 343
[117]: Shimpi A.L., Intel Iris Pro 5200 Graphics Review: Core i7-4950HQ Tested, AnandTech,
June 1 2013, http://www.anandtech.com/show/6993/intel-iris-pro-5200-graphics-
review-core-i74950hq-tested
[118]: Product Brief Intel Xeon Processor E3-1200 v2 Product Family, 2012,
http://software.intel.com/sites/products/vcsource/files/xeon-e3-1200v2-brief__2_.pdf
[119]: Leberecht M., Expanding Intel Architecture Flexibility in the Data Center, March 20 2013,
http://www.worldhostingdays.com/downloads/2013/hStag2a1.pdf
[120]: Wikipedia: Haswell (microarchitecture),
http://en.wikipedia.org/wiki/Haswell_%28microarchitecture%29
[121]: Von Holzbauer F., Kugler A., Neue Intel-Architektur mit Grafik-Fokus, Chip Online,
June 1 2013, http://www.chip.de/artikel/Intel-Haswell-Neue-CPUs-fuer-Notebooks-und-
PCs_62209040.html
[122]: Valentine B., Intel Next Generation Microarchitecture Codename Haswell: New Processor
Innovations, 2012, http://ftp.software-sources.co.il/Processor_Architecture_Update-
Bob_Valentine.pdf
[124]: Scansen D., Intel Launches Next Generation of Microprocessors, Engineering, June 10 2013,
http://www.engineering.com/ElectronicsDesign/ElectronicsDesignArticles/ArticleID/
5838/Intel-Launches-Next-Generation-of-Microprocessors.aspx
[123]: Brown M., Intel lifts the veil on Haswell graphics, PC World, May 2 2013,
http://www.pcworld.com/article/2037063/intel-lifts-the-veil-on-haswell-graphics.html
References (14)

## Slide 344
[125]: Walton J., Hit the Road, Jack: Intel’s Mobile Quad-Core Haswell SKUs, AnandTech,
June 1 2013, http://www.anandtech.com/show/7002/hit-the-road-jack-intels-mobile-
quadcore-haswell-skus
[126]: Walton J., Intel’s Haswell: Quad-Core Desktop Processor SKUs, AnandTech, June 1 2013,
http://www.anandtech.com/show/7001/intels-haswell-quadcore-desktop-processor-skus
[127]: Kirsch N., Intel Core i7-4770K Haswell Processor Performance Review Posted, Legit Reviews,
March 18 2013, http://www.legitreviews.com/intel-core-i7-4770k-haswell-processor-
performance-review-posted_15286
[128]: Kennedy P., Intel Xeon E3-1200 V3 Series Compute Value Comparison, STH, June 13 2013,
http://www.servethehome.com/intel-xeon-e3-1200-v3-series-compute-comparison/
[129]: Kennedy P., Leaked Intel Xeon E3-1200 V3 Series and Comparison to V1 and V2, STH,
April 3 2013, http://www.servethehome.com/leaked-intel-xeon-e3-1200-v3-series-
comparison-v1-v2/
[130]: Intel® Xeon® Processor E3-1200 v3 Product Family with Intel® HD Graphics P4600 and
Intel® C226 Chipset: Block Diagram, http://www.intel.com/content/www/us/en/
intelligent-systems/denlow/xeon-e3-1200-v3-c266-chipset-ibd.html
[132]: Intel Core i7 High End Desktop Processor Family for Socket LGA-2011, Aug. 2013,
[131]: Chiappetta M., Intel Core i7-4960X Ivy Bridge-E CPU Review, Hot Hardware,
Sept. 3 2013, http://hothardware.com/Reviews/Intel-Core-i74690X-Extreme-Edition-
Ivy-Bridge-E-CPU-Review/?page=2
References (15)

## Slide 345
[133]: Pop S., Intel Releases Core i7 Extreme Central Processing Units, Softpedia, Sept. 9 2013,
http://news.softpedia.com/news/Intel-Releases-Core-i7-Extreme-Central-Processing-
Units-381369.shtml
[134]: Shimpi A.L., Intel Core i7 4960X (Ivy Bridge E) Review, AnandTech, Sept. 3 2013,
http://www.anandtech.com/show/7255/intel-core-i7-4960x-ivy-bridge-e-review
[135]: Hruska J., Core i7-4960X Ivy Bridge-E review: Intel’s Great Limp Forward, ExtremeTech,
Sept. 3 2013, http://www.extremetech.com/gaming/165498-core-i7-4960x-ivy-bridge-e-
review-intels-great-limp-forward
[136]: Novakovic N., Intel Xeon 2013 update – A bit later, but a bit better too, VR-Zone,
April 9 2013, http://vr-zone.com/articles/intel-xeon-2013-update--a-bit-later-but-a-bit-
better-too/19581.html?utm_source=feedburner&utm_medium=feed&utm_campaign=
Feed%3A+TheTomorrowTimes+%28The+Tomorrow+Times%29
[137]: De Gelas J., Intel's Xeon E5-2600 V2: 12-core Ivy Bridge EP for Servers, AnandTech,
Sept. 17 2013, http://www.anandtech.com/show/7285/intel-xeon-e5-2600-v2-12-core-
ivy-bridge-ep
[139]: Eshelman E., Intel Xeon E5-2600v2 “Ivy Bridge” Processor Review, Microway,
Sept. 10 2013, http://www.microway.com/hpc-tech-tips/intel-xeon-e5-2600v2-ivy-
bridge-processor-review/
[138]: Morgan T.P., Intel carves up Xeon E5-2600 v2 chips for two-socket boxes, The Register,
Sept. 10 2013, http://www.theregister.co.uk/2013/09/10/intel_ivy_bridge_xeon_e5_
2600_v2_launch/
References (16)

## Slide 346
[140]: Shvets A., Intel Xeon E5-1600 v2 and E5-2600 v2 CPUs launched, CPU World,
Sept. 14 2013, http://www.cpu-world.com/news_2013/2013091401_Intel_Xeon_
E5-1600_v2_and_E5-2600_v2_CPUs_launched.html
[141]: Mujtaba H., Intel Ivy Bridge-EX Confirmed To Feature 15 Cores – Arrives in 2H 2013,
WCCF Tech, 2013, http://wccftech.com/intel-ivy-bridge-ex-feature-15-cores/
[142]: Shvets G., Some details of upcoming Intel Xeon E5 v2 and E7 v2 CPUs, CPU World,
April 2 2013, http://www.cpu-world.com/news_2013/2013040201_Some_details_of_
upcoming_Intel_Xeon_E5_v2_and_E7_v2_CPUs.html
[143]: Mouthaan M., Intel Haswell-E slides published; DDR4 and octa-cores, Hardware Info,
June 16 2013, http://us.hardware.info/news/35581/intel-haswell-e-slides-published-
ddr4-and-octa-cores
[144]: Introducing the 4th Generation Intel Core Processor (code-named Haswell), 2013,
http://software.intel.com/sites/default/files/introduction-to-intel-4th-generation-core-
processor.pdf
References (17)
[145]: Unparalleled Performance and Responsiveness, Product Brief, Intel Z87 Chipset, 2013,
http://www.intel.com/content/dam/www/public/us/en/documents/product-briefs/
z87-chipset-brief.pdf
[146]: Haas, J. & Vogt P., Fully buffered DIMM Technology Moves Enterprise Platforms to the
Next Level,” Technology Intel Magazine, March 2005, pp. 1-7
Intel Xeon processor E3-1200 v3 Product Family and the Emergence of Graphics in the
Cloud, June 3 2013,
http://www.yumpu.com/en/document/view/18758369/cover-slide-title-intel-newsroom
[147]:

## Slide 347
[148]: Gasior G., Leaked slides expose Haswell's integrated voltage regulator, May 13, 2013,
http://techreport.com/news/24802/leaked-slides-expose-haswell-integrated-voltage-
regulator
References (18)
[149]: Hammerlund P. & al., Haswell: The Fourth Generation Intel Core Processor, IEEE MICRO
March/April 2014, pp. 6-20
[150]: Burton E.A. & al., FIVR – Fully Integrated Voltage Regulators on 4th Generation Intel
Core™ SoCs, Proc. Twenty-Ninth Annual IEEE Applied Power Electronics Conference and
Exposition (APEC), 2014, pp. 432 - 439
[151]: Application Note: Atmel AT04204: Design a Buck Converter with XMEGA E, Atmel Corp.
2013, http://www.atmel.com/Images/Atmel-42183-Design-a-Buck-Converter-with-
XMEGA-E_AP-Note_AT04204.pdf
[152]: Buck converter, http://en.wikipedia.org/wiki/Buck_converter
[153]: Borkar R., A Multy Year Journey, Aug. 11 2014, Intel,
http://download.intel.com/newsroom/kits/14nm/pdfs/Intel_14nm_New_uArch.pdf
[154]: Bohr M., 14 nm Technology Announcement, Aug. 11 2014, Intel,
http://download.intel.com/newsroom/kits/14nm/pdfs/Intel_14nm_New_uArch.pdf
[155]: Jourdan S., Broadwell Microarchitecture Disclosure, Aug. 11 2014, Intel,
http://download.intel.com/newsroom/kits/14nm/pdfs/Intel_14nm_New_uArch.pdf
[156]: Chennupaty S., Jiang H., Sreenivas A., Technology insight: Intel’s Next Generation 14 nm
Microarchitecture for Client and Server, IDF 2014 SPCS002, San Francisco, 2014,
https://intel.activeevents.com/sf14/connect/sessionDetail.ww?SESSION_ID=1204

## Slide 348
[158]: Smith S.L., Intel Strategy & Technology Update, Barclays Capital Global Technology Conf.,
Dec. 2011, http://files.shareholder.com/downloads/INTC/1576180143x0x526852/c9868a
3a-494e-4506-bcc6-a631aca1fd75/Steve%20Smith%20Barclays%20Dec%202011.pdf
[159]: Kanter D., Intel’s merom Unveiled, Real World Technologies, March 9, 2006,
http://www.realworldtech.com/merom/6/
[160]: Kanter D., Inside Barcelona: AMD's Next Generation, Real World Technologies, May 9, 2007,
http://www.hypertransport.org/docs/news/rwtech_inside_barcelona_05-16-07.pdf
[161]: - Intel 64 and IA-32 Architectures Software Developer’s Manual Combined Volumes:
1, 2A, 2B, 2C, 3A, 3B and 3, Intel, Order Number: 325462-052US, September 2014,
http://www.intel.com/content/dam/www/public/us/en/documents/manuals/64-ia-32-
architectures-software-developer-manual-325462.pdf
[162]: - SSE, The Free Dictionary, http://encyclopedia2.thefreedictionary.com/Supplemental+SSE3
[163]: Doweck J., Inside Intel Core Microarchitecture, Hot Chips 18, 2006,
http://www.hotchips.org/wp-content/uploads/hc_archives/hc18/3_Tues/HC18.S9/
HC18.S9T4.pdf
[164]: Goto H., ARM Cortex – A Family Architecture, 2010,
http://pc.watch.impress.co.jp/video/pcw/docs/423/409/p1.pdf
References (19)
[157]: Junkins S., The Compute Architecture of Intel Processor Graphics Gen8, IDF 2014,
https://software.intel.com/sites/default/files/managed/71/a2/Compute%20Architecture%
20of%20Intel%20Processor%20Graphics%20Gen8.pdf
[165]: Kuppuswamy, R. C al., Over one million TPCC with a 45nm 6-core Xeon® CPU,
IEEE International Solid-State Circuits Conference - Digest of Technical Papers,
ISSCC 2009, Feb. 2009, pp. 70 - 71,71a

## Slide 349
[167]: Shimpi A. L., Intel’s Core i7 870 C i5 750 Lynnfield: Harder, Better, Faster, Stronger,
AnandTech, Sept. 8, 2009, http://www.anandtech.com/show/2832/2
References (20)
[168]: Lomont C., Introduction to Intel® Advanced Vector Extensions, Intel, 23 May 2011,
https://software.intel.com/sites/default/files/m/d/4/1/d/8/Intro_to_Intel_AVX.pdf
[169]: Intel QuickPath Interconnect Electrical Architecture Overview, Intel, 2010,
http://jamesstovalldesign.files.wordpress.com/2012/08/pages-from-intel_qpied_final_
03-18-10.pdf
[170]: Davis L., PCI Express Bus,
http://www.interfacebus.com/PCI-Express-Bus-PCIe-Description.html
[171]: Wasson S., Intel's Xeon E5-2687W v3 processor reviewed, TechReport, Sept. 8 2014,
http://techreport.com/review/27018/intel-xeon-e5-2687w-v3-processor-reviewed
[172]: Klemm M., The Intel Platform for High Performance Computing, Intel, Oct. 07 2014
https://sharepoint.campus.rwth-aachen.de/units/rz/HPC/public/Shared%20Documents/
2014-10-07_aiXcelerate-01_Intel_Architecture-Haswell+Xeon_Phi.pdf
[173]: Moen M., Ragland D., Guerrero JJ., Overclocking Unlocked Intel Core Processors for
High Performance Gaming and Content Creation, IDF 2013, San Francisco, Sept. 1 2013,
AIOS001
[165]: Borges L., Intel Technologies for High Performance Computing, Intel Software Solution
Conference 2014 Brazil, May 2014,
http://www.slideshare.net/IntelSoftwareBR/hpc-update-istep2014
[166]: Intel Core 2 Duo Processor, http://www.intel.com/pressroom/kits/core2duo/

## Slide 350
[174]: Wikipedia, Intel HD and Iris Graphics,
https://en.wikipedia.org/wiki/Intel_HD_and_Iris_Graphics
[175]: Intel Xeon Processor E3-1200 Product Family, Product Brief, 2011
[176]: Cutress I., The Intel Haswell Refresh Review: Core i7-4790, i5-4690 and i3-4360 Tested,
AnandTech, May 11 2014, http://www.anandtech.com/show/7963/the-intel-haswell-
refresh-review-core-i7-4790-i5-4690-and-i3-4360-tested/2
[177]: Altavilla D., Intel 5th Gen Core Series Mobile Processors A Huge Deal For Thin And Light
Notebooks, Forbes, Jan. 8 2015, http://www.forbes.com/sites/davealtavilla/2015/01/08/
intel-5th-gen-core-series-mobile-processors-a-huge-deal-for-thin-and-light-notebooks/
[178]: Campbell M., Intel to Bring back FIVR after Skylake and Kaby Lake CPUs, Overclock 3D,
July 13 2015, http://www.overclock3d.net/articles/cpu_mainboard/intel_to_bring_
back_fivr_after_skylake_and_kaby_lake_cpus/1
[179]: Howse B., Smith R., Tick Tock On The Rocks: Intel Delays 10nm, Adds 3rd Gen 14nm Core
Product "Kaby Lake„, AnandTech, July 16 2015,
http://www.anandtech.com/show/9447/intel-10nm-and-kaby-lake
[181]: Cutress I., The Intel Broadwell Desktop Review: Core i7-5775C and Core i5-5675C Tested
(Part 1), AnandTech, June 2 2015,
http://www.anandtech.com/show/9320/intel-broadwell-review-i7-5775c-i5-5675c
[180]: Intel's (INTC) CEO Brian Krzanich on Q2 2015 Results - Earnings Call Transcript, Seeking
Alpha, July 15 2015, http://seekingalpha.com/article/3329035-intels-intc-ceo-brian-
krzanich-on-q2-2015-results-earnings-call-transcript?page=2
References (21)

## Slide 351
[182]: Johnson H., Voltage-Regulator Droop, Signal Consulting, Sept. 14 2006,
http://www.sigcon.com/Pubs/edn/VoltageRegulatorDroop.htm
[183]: Chennupaty S., Jiang H., Intel’s 14 nm Microarchitecture (Broadwell), IDF15
[184]: Hux A, 5th Generation Intel Core Processor Graphics: Gen8 Compute Architecture,
IDF15, GVCS001
[185]: Woligroski D., Intel's Broadwell Core M Processor: New Details, SKUs and Specifics,
Tom’s Hardware, Sept. 5 2014,
http://www.tomshardware.com/news/intel-broadwell-core-m,27596.html
[186]: Mujtaba H., Intel’s 14nm Core M Series “Broadwell-Y” Processors With 4.5W TDP Detailed –
Powers Fanless and 2 in 1 Mobility Devices, WCCF Tech, 2014,
http://wccftech.com/intel-14nm-core-m-broadwell-y-processors-detailed/
[187]: Cutress I., Intel Releases Broadwell-U: New SKUs, up to 48 EUs and Iris 6100, AnandTech,
Jan. 5 2015, http://www.anandtech.com/show/8814/intel-releases-broadwell-u-new-
skus-up-to-48-eus-and-iris-6100/4
[189]: Intel Z97 Chipset Platform Diagram, http://www.intel.com/content/www/us/en/chipsets/
performance-chipsets/z97-chipset-diagram.html
[188]: Cutress I., Intel Launches Five 47W Laptop Broadwell SKUs, AnandTech, June 2 2015,
http://www.anandtech.com/show/9326/intel-launches-five-47w-laptop-broadwell-skus
References (22)
[190]: Detalles de los procesadores Intel “Skylake-S” (6° Gen), Taringa, March 2 2015,
http://www.taringa.net/posts/info/18522818/Detalles-de-los-procesadores-Intel-
Skylake-S-6-Gen.html

## Slide 352
[191]: Nguyen C., Intel's Skylake expected to bring stamina and speed to your laptop,
Techradar, 2015, http://www.techradar.com/news/computing-components/processors/
intel-s-skylake-processors-expected-to-bring-stamina-and-speed-to-your-laptop-1300173
[192]: Shilov A., Intel ‘Skylake’ launch schedule revealed: CPUs to arrive in August, Kit Guru,
May 21 2015, http://www.kitguru.net/components/cpu/anton-shilov/complete-intel-
skylake-launch-schedule-revealed-chips-to-be-showcased-in-august/
[193]: Novakovic N., Intel’s 2015 Roadmap Conundrum: Tick-Tock is Not a Swiss Clock, VR World,
May 31 2015, http://www.vrworld.com/2015/05/31/intels-2015-roadmap-conundrum-
tick-tock-is-not-a-swiss-clock/
[194]: Mujtaba H., Intel 14nm Kaby Lake “Skylake Refresh” Platform Detailed – Launching in
2H 2016, 256 MB eDRAM H-Series and 91W K-Series Unveiled, WCCF Tech, 2015,
http://wccftech.com/intel-14nm-kaby-lake-haswell-refresh-platform-detailed-launching-
2h-2016-256-mb-edram-hseries-91w-kseries-unveiled/#ixzz3hczeTsOH
References (23)
[196]: Blythe D., Technology Insight: Next Generation Intel Processor Graphics Architecture
Code Name Skylake, SPCS003, IDF15, San Francisco, Aug. 2015
[195]: Gianos C., Intel Xeon Processor E5-2600 v3 Product Family Architectural Overview ,
Nov. 16 2014
[197]: Kanter D., Intel’s Ivy Bridge Graphics Architecture, Real World Technologies, April 22 2012,
http://www.realworldtech.com/ivy-bridge-gpu/2/
[198]: Rotem E., Intel Architecture, Code Name Skylake, Deep Dive: A New Architecture to Manage
Power Performance and Energy Efficiency, IDF15, San Francisco, Aug. 2015

## Slide 353
[199]: Junkins S., The Compute Architecture of Intel Processor Graphics Gen7.5, Aug. 1 2014,
https://software.intel.com/sites/default/files/managed/f3/13/Compute_Architecture_of_
Intel_Processor_Graphics_Gen7dot5_Aug2014.pdf
[200]: Mandelblat J., Technology Insight: Intel’s Next Generation Microarchitecture, Code Name
Skylake, IDF15, San Francisco, Aug. 2015
[201]: Bright P., The many tricks Intel Skylake uses to go faster and use less power, Ars Technica,
Aug. 19 2015, http://arstechnica.com/information-technology/2015/08/the-many-
tricks-intel-skylake-uses-to-go-faster-and-use-less-power/
[202]: Cutress I., The Intel Skylake Mobile and Desktop Launch, with Architecture Analysis,
AnandTech, Sept. 1 2015, http://www.anandtech.com/show/9582/intel-skylake-mobile-
desktop-launch-architecture-analysis
References (24)
[203]: Chester E., Intel Skylake review: Core i7-6700K and Core i5-6600K review, Trusted Reviews,
Aug. 5 2015, http://www.trustedreviews.com/intel-skylake-review-core-i7-6700k-and-
core-i5-6600k-review#O6vSUh2MV2ptOwqm.99
[204]: Torres A., 4th Generation Intel Core Processor Family, Press Briefing, Spring 2013
[205]: Wikipedia, Haswell (microarchitecture),
https://en.wikipedia.org/wiki/Haswell_(microarchitecture)
[206]: Hollister S., Intel’s New Skylake Processors: What You Need To Know, Gizmodo,
Sept. 5 2015, http://gizmodo.com/intels-new-skylake-processors-what-you-need-to-
know-1728020921

## Slide 354: References (25)
[207]: Rotem E., Naveh A., Rajwan D., Ananthakrishnan A. & Weissmann E., Power management
architecture of the 2nd generation Intel® Core microarchitecture, formerly codenamed
Sandy Bridge, Hot Chips, Aug. 2011,
http://www.hotchips.org/wp-content/uploads/hc_archives/hc23/HC23.19.9-Desktop-
CPUs/HC23.19.921.SandyBridge_Power_10-Rotem-Intel.pdf
[208] - Intel "Skylake" Die Layout Detailed, TechPowerUp, 18.08.2015,
http://www.techpowerup.com/215333/intel-skylake-die-layout-detailed.html
[209] Singhal R., Next Generation Intel Microarchitecture (Nehalem) Family: Architecture Insight
and Power Management, IDF Taipeh, Oct. 2008,
http://intel.wingateweb.com/taiwan08/published/sessions/TPTS001/FA08%20IDF
-Taipei_TPTS001_100.pdf
[210]: Enhanced Intel® SpeedStep Technology for the Intel® Pentium M Processor, White Paper,
March 2004, http://download.intel.com/design/network/papers/30117401.pdf
[211]: Schilling A., Intel axes Fully Integrated Voltage Regulator for 'Skylake' and 'Kaby Lake',
HardwareLuxx, 08 July 2015,
http://www.hardwareluxx.com/index.php/news/hardware/cpu/36000-intel-axes-fully-
integrated-voltage-regulator-for-skylake-and-kaby-lake.html
[212]: Karedla R., Intel Xeon E5-2600 v3 (Haswell) Architecture & Features, Intel, 2014,
http://repnop.org/pd/slides/PD_Haswell_Architecture.pdf
[213]: Gwennap : L., Sandy Bridge Spans Generations, Microprocessor, 9/27/10,
http://www.cs.nyu.edu/courses/fall13/CSCI-GA.3033-008/Microprocessor-Report-
Sandy-Bridge-Spans-Generations-243901.pdf

## Slide 355: References (25)
[214]: Stokes J., Inside the Machine, ars Technica Library, No Starch Press, san Francisco, 2007
[215]: Kuppuswamy, R. C al., Over one million TPCC with a 45nm 6-core Xeon® CPU,
IEEE International Solid-State Circuits Conference - Digest of Technical Papers,
ISSCC 2009, Feb. 2009, pp. 70 - 71a
[216]: Smith R., Intel's Changing Future: Smartphone SoCs Broxton & SoFIA Officially Cancelled,
AnandTech, April 29, 2016,
http://www.anandtech.com/show/10288/intel-broxton-sofia-smartphone-socs-cancelled
[217]: Qualcomm dominates smartphone chip and baseband, tablet processor markets, Mobile
Europe, February 17 2014
http://www.mobileeurope.co.uk/Press-Wire/qualcomm-dominates-smartphone-chip-and
-baseband-tablet-processor-markets
[218]: Howse B., Examining Intel's New Speed Shift Tech on Skylake: More Responsive Processors
AnandTech, November 6, 2015,
http://www.anandtech.com/show/9751/examining-intel-skylake-speed-shift-more-
responsive-processors
[219]: Ready to test your browser's performance?, Principled Technologies, 2016,
http://www.principledtechnologies.com/benchmarkxprt/webxprt/run-webxprt-mobile
[220]: Server duel: Xeon Woodcrest vs. Opteron Socket F, Tweakers, 7 Sept. 2006,
http://tweakers.net/reviews/646/2/server-duel-xeon-woodcrest-vs-opteron-socket-f-
post-mortem-netburst.html