## Slide 1
Dezső Sima
October 2017
(Ver. 1.0)
 Sima Dezső, 2017
Intel’s High-End
Server Processors and Platforms

## Slide 2
Intel’s high-end 4S/8S server processors and platforms
1. Introduction to Intel’ s high-end multicore
4S/8S server platforms
2. Evolution of Intel’s high-end multicore
4S/8S server platforms
5. References
3. Example 1: The Brickland platform
4. Example 2: The Purley platform
Notes: 2

## Slide 3: Intel’s high performance MP platforms
Remark
The material presented in these slides is restricted to Intel’s high-end multicore x86 server
(called Xeon) processors and platforms, accordingly, previous and IA64 (Itanium) based
processors and systems are not covered.
Intel's server families
Xeon servers
Itanium servers
x86 ISA
(1998 - recently)
IA-64 ISA
(2001 - 2017)
Intel's first multicore server processors were based on the 3. core of the Pentium 4 family
(called Prescott), there were introduced about 2005.

## Slide 4
Introduction to Intel’s high-end multicore
4S/8S server platforms
1.1 The worldwide server market
1.2 The platform concept
1.3 Server platforms classified according to their
scalability
1.4 Multiprocessor server platforms classified
according to their memory architecture
1.5 Platforms classified according to the
number of chips constituting the chipset
1.6 Naming scheme of Intel’s server processors
1.7 Overview of Intel’s high-end 4S/8S server platforms
with multicore processors
Notes: 4

## Slide 5
1.1 The worldwide server market
Notes: 5

## Slide 6: 1.1 The worldwide server market (1)
Recent market share of 1S and 2S servers [170]
Introduction to Intel’s high-end multicore 4S/8S server platforms
1.1 The worldwide server market (1)

## Slide 7: 1.1 The worldwide server market (2)
The worldwide 4S (4-socket) server market [52]
*
MSS: Market Segment Share

## Slide 8: 1.1 The worldwide server market (3)
Remark
In 06/2017 AMD launched their Epyc server processor line supporting at its introduction
2-socket configurations.
Epyc server processors are based on the Zen microarchitecture.
Time will show how far AMD will be able to gain market share against Intel's latest,
Skylake-SP based servers.
*

## Slide 9: 1.1 The worldwide server market (4)
Vendor | 1Q16 Revenue | 1Q16 Market Share | 1Q16/1Q15 Revenue Growth
1. HP | $3,306.8 | 26.7% | 3.5%
2. Dell | $2,267.8 | 18.3% | -1.8%
3. IBM | $1,139.5 | 9.2% | -32.9%
4. Lenovo * | $871.2 | 7.0% | -8.6%
5. Cisco * | $850.2 | 6.9% | -4.5%
ODM Direct | $863.8 | 7.0% | -11.0%
Others | $3,082.4 | 24.9% | 9.0%
Total | $12,382 | 100% | -3.6%
Top 5 worldwide server systems vendor revenues, market shares and growth, Q1 2016,
(Revenues are in Millions USD) [137]
HPE: HP Enterprise
Source: IDC's Worldwide Quarterly Server Tracker, June 2016

## Slide 10
1.2 The platform concept
Notes: 10

## Slide 11: 1.2 The platform concept (1)
1.2 The platform concept
The notion platform is widely used in different segments of the IT industry e.g. by
IC manufacturers, system providers or even by software suppliers with different interpretations.
Here we are focusing on the platform concept as used by system providers, like Intel or AMD.
The platform is defined by the main components of the system architecture, being typically
The platform concept of system providers
Remark
The designation platform is often understood as the entire system architecture.
the processor or processors (in multiprocessors)
the related chipset as well as
the interfaces (buses) interconnecting them.
*

## Slide 12: 1.2 The platform concept (2)
Core 2 (2C)
E5000 MCH
(Enhanced)
631xESB/ 632xESB IOH
FSB
Core 2 (2C)
FBDIMM
w/DDR2-533
ESI
1333/1067 MT/s
Example 1: A simple traditional 2S server platform
2S: Dual Socket

## Slide 13: 1.2 The platform concept (3)
Example 2: A recent 4S platform
(The Brickland 4S/8S server platform with Haswell-EX processors (2015)
ME: Management Engine
QPI 1.1: Up to 9.6 GT/s
QPI
1.1
QPI
1.1
QPI 1.1
QPI 1.1
QPI 1.1
QPI 1.1
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI2
channels
2x4 SMI2
channels
Xeon E7-8800 v3
(Haswell-EX)
Haswell-EX 18C
Haswell--EX 18C
Haswell-EX 18C
Haswell-EX 18C
SMI2: Scalable Memory Interface 2
(Parallel 64-bit VMSE data link between
the processor and the SMB)
SMB: Scalable Memory Buffer
(C112/C114: Jordan Creek 2)
(Performs conversion between the
parallel SMI2 and the parallel
DDR3/DDR4 DIMM interfaces)
C112: 2 DIMMs/channel
C114: 3 DIMMs/channel
Up to DDR3-1600
in both performance and lockstep modes and
up to DDR4-1866 in lockstep mode
PCIe 3.0
32
PCIe 3.0
32
C602J PCH
(Patsburg J)
DMI2
4xPCIe2
ME
PCIe 3.0
32
PCIe 3.0
32

## Slide 14: 1.2 The platform concept (4)
Compatibility of platform components (2)
Since platform components are connected via specified interfaces to build an entity, called
platform, platform components, such as processors or memories are compatible to a given
platform as long as they have the same interfaces (including interface parameters, such as
transfer rates etc.).
*

## Slide 15: 1.2 The platform concept (5)
Nehalem-EX 8C
Westmere-EX 10C
7500 IOH
QPI
QPI
QPI
QPI
QPI
QPI
QPI
QPI
SMB
SMB
Nehalem-EX: up to DDR3-1067
Westmere-EX: up to DDR3-1333
SMB
SMB
SMB
SMB
SMB
SMB
ICH10
ESI
SMI: Scalable Memory Interface
(Serial link between the processor
and the SMB)
SMB: Scalable Memory Buffer
(Performs conversion between the
serial SMI and the parallel
DDR3 DIMM interfaces)
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI
channels
2x4 SMI
channels
Example: Interface requirements for compatible platform components
ME
ME: Management Engine
Xeon 7500
(Nehalem-EX)
(Becton) 8C
Xeon E7-8800
(Westmere-EX) 10C
Nehalem-EX 8C
Westmere-EX 10C
Nehalem-EX 8C
Westmere-EX 10C
Nehalem-EX 8C
Westmere-EX 10C
/
Figure: The Boxboro-EX MP server platform supporting Nehalem-EX/Westmer-EX server processor
2 DIMMs/memory channel
4 x QPI up to 6.4 GT/s
36
PCIe
2.0

## Slide 16
Platform/ Scalability | Core | Techn. | Intro. | High-end 4S/8S server processor lines | Core count | Chipset | Proc. socket
Truland MP (4S) | Pentium 4 MP Prescott | 90 nm | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 1C | E8500 + ICH5 | LGA 604
 | Pentium 4 Presc. | 90 nm | 11/2005 | 7000 (Paxville MP) | 2x1C | E8501 + ICH5 | 
 | Pentium 4 Presc. | 65 nm | 8/2006 | 7100 (Tulsa) | 2x1C |  | 
Caneland (4S) | Core2 | 65 nm | 9/2007 | 7200 (Tigerton DC) 7300 (Tigerton QC) | 2C 2x2C | E7300 (Clarksboro)+ 631x/632x ESB | LGA 604
 | Penryn | 45 nm | 9/2008 | 7400 (Dunnington) | 6C |  | 
Boxboro-EX (8S) | Nehalem | 45 nm | 3/2010 | 7500 (Beckton/ Nehalem-EX) | 8C | 7500 (Boxboro) + ICH10 | LGA 1567
 | Westmere | 32 nm | 4/2011 | E7-8800 (Westmere-EX) | 10C |  | 
 | Sandy Bidge | 32 nm |  |  |  |  | 
Brickland (8S) | Ivy Bridge | 22 nm | 2/2014 | E7-8800 v2 (Ivy Bridge-EX) | 15C | C602J (Patsburg J) | LGA 2011-1
 | Haswell | 22 nm | 5/2015 | E7-8800 v3 (Haswell-EX) | 18C |  | 
 | Broadwell | 14 nm | 6/2016 | E7-8800 v4 (Broadwell-EX) | 24C |  | 
Purley (2S/4S/8S) | Skylake | 14 nm | 7/2017 | Platinum 8100 (Skylake-SP) | 28C | C620 (Lewisburg) | LGA 3647
Overview of Intel’s high-end 4S/8S multicore server platforms and processors
1.2 The platform concept (6)

## Slide 17
1.3 Server platforms classified according to their scalability
Notes: 17

## Slide 18: 1.3 Server platforms classified according to their scalability (1)
1.3 Server platforms classified according to their scalability
2S (DP)
server platforms
Server platforms
Platforms for more than 4 or 8 sockets
2- processor server platforms
(2-socket server platforms)
4S/8S (MP)
server platforms
4/8-processor server platforms
(4/8-socket server platforms)
Server platforms for
more than the Intel
supported number of
sockets
(4 or 8 sockets)
They need third party
node controllers
Uniprocessor server platforms
(UP-server platforms)
1-processor server platforms
(1-socket server platforms)
Multiprocessor server platforms
Server platforms supporting more than one processor
(Multi-socket server platforms)
Truland-MP platform
Caneland MP platform and
4S platforms
8S platforms
E5-4600, v2, v3, v4
E7-4800, v2, v3, v4
subsequent platforms with
processors
Platforms with
E7-8800, v2, v3, v4
processors
E5-2600, v2, v3, v4
E7-2800, v2,
platforms with
processors
Early DP platforms and
*

## Slide 19
1.4 Multiprocessor server platforms classified according to
their memory architecture
Notes: 19

## Slide 20: 1.4 Multiprocessor server platforms classified according to their memory arch. (1)
1.4 Multiprocessor server platforms classified according to their memory architecture (1)
SMPs
(Symmetrical MultiProcessor)
Multiprocessor server platforms
classified according to their memory architecture
NUMAs
Multiprocessors (Multi socket system)
with Non-Uniform Memory Access
Multiprocessors (Multi socket system)
with Uniform Memory Access (UMA)
Typical examples
Processor
MCH
ICH
FSB
Processor
E.g. DDR2-533
ESI
E.g. DDR3-1333
Processor
IOH1
QPI
QPI
ICH
ESI
QPI
E.g. DDR3-1333
Processor
All processors access main memory by the same
mechanism, (e.g. by individual FSBs and an MCH).
1ICH: I/O hub
ESI: Enterprise System Interface
*
Each processor is allocated a part of the main memory
(with the related memory space), called the local memory,
whereas the rest is considered as the remote memory.

## Slide 21: 1.4 Multiprocessor server platforms classified according to their memory arch. (2)
SMPs
(Symmetrical MultiProcessor)
NUMAs
All processors share the same memory space.
All processors share the same memory space.
Multiprocessor server platforms
classified according to their memory architecture
Main features of SMP-type and NUMA-type server platforms
Consequently, all processors access memory
basically with the same latency.
The local part of the main memory can be accessed
by each processor immediately, e.g. via their private
on-die memory controller,
whereas remote parts of the main memory will be
accessed via the processor owing the requested
memory part.
Processors access their local memory space
with a significantly shorter latency than their
remote memory space, consequently, processors
access main memory with different latencies.
*

## Slide 22: 1.4 Multiprocessor server platforms classified according to their memory arch. (3)
Example of measured read latencies of uncached data [73]
Read latencies depend on whether referenced data is kept in the own or remote main memory space.
a) Read latency of uncached data when referenced data is kept in the own memory space
Read latency:
65.1 ns (190 cycles)
IMC: Integrated Memory Controller

## Slide 23: 1.4 Multiprocessor server platforms classified according to their memory arch. (4)
b) Read latency of uncached data when referenced data is kept in the remote memory space [73]
Read latency:
106 ns (~310 cycles)
Read latency is increased now by the inter-processor access penalty of 41 ns in this case.

## Slide 24
1.5 Platforms classified according to the number of chips
constituting the chipset
Notes: 24

## Slide 25: 1.5 Platforms classified according to the number of chips constituting the chipset (1)
Three-chip implementation
Implementation of platforms
classified according to the number of chips constituting the chipset
Two-chip implementation
The system architecture consists
basically of three chip types
(processors/MCH/ICH)
The system architecture consists
basically of two chip types
(processors/PCH)
1.5 Classification of platforms according to the number of chips constituting
the chipset
Truland platform (2005/2006)
Caneland platform (2007/2008)
Boxboro-EX platform (2010/2011)
Brickland platform (2014/2015)
Purley platform (2017)
Single-chip implementation
The PCH is integrated
on the die (or package)
(AMD's 2S EPYC-7000
series processors)
*

## Slide 26: 1.5 Platforms classified according to the number of chips constituting the chipset (2)
Nehalem-EX 8C
Westmere-EX 10C
7500 IOH
QPI
QPI
QPI
QPI
QPI
QPI
QPI
QPI
SMB
SMB
Nehalem-EX: up to DDR3-1067
Westmere-EX: up to DDR3-1333
SMB
SMB
SMB
SMB
SMB
SMB
ICH10
ESI
SMI: Scalable Memory Interface
(Serial link between the processor
and the SMB)
SMB: Scalable Memory Buffer
(Performs conversion between the
serial SMI and the parallel
DDR3 DIMM interfaces)
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI
channels
2x4 SMI
channels
Example of a 3-chip platform: The Boxboro-EX 4S/8S server platform supporting
Nehalem-EX/Westmere-EX processors
ME
ME: Management Engine
Xeon 7500
(Nehalem-EX)
(Becton) 8C
Xeon E7-4800
(Westmere-EX) 10C
Nehalem-EX 8C
Westmere-EX 10C
Nehalem-EX 8C
Westmere-EX 10C
Nehalem-EX 8C
Westmere-EX 10C
/
Nehalem-EX aimed Boxboro-EX MP server platform (for up to 10 C)
2 DIMMs/memory channel
4 x QPI up to 6.4 GT/s
36
PCIe
2.0

## Slide 27: 1.5 Platforms classified according to the number of chips constituting the chipset (3)
Example of a 2-chip platform: The Brickland-EX 4S/8S server platform supporting
Ivy Bridge-EX/Haswell-EX/Broadwell-EX processors
ME: Management Engine
QPI 1.1: Up to 9.6 GT/s
QPI
1.1
QPI
1.1
QPI 1.1
QPI 1.1
QPI 1.1
QPI 1.1
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI2
channels
2x4 SMI2
channels
Xeon E7-8800 v2/v3/v4
(Ivy Bridge-EX / Haswell-EX /Broadwell-EX)
Haswell-EX 18C
Haswell--EX 18C
Haswell-EX 18C
Haswell-EX 18C
SMI2: Scalable Memory Interface 2
(Parallel 64-bit VMSE data link between
the processor and the SMB)
SMB: Scalable Memory Buffer
(C112/C114: Jordan Creek 2)
(Performs conversion between the
parallel SMI2 and the parallel
DDR3/DDR4 DIMM interfaces)
C112: 2 DIMMs/channel
C114: 3 DIMMs/channel
Up to DDR3-1600
in both performance and lockstep modes and
up to DDR4-1866 in lockstep mode
PCIe 3.0
32
PCIe 3.0
32
C602J PCH
(Patsburg J)
DMI2
4xPCIe2
ME
PCIe 3.0
32
PCIe 3.0
32

## Slide 28
1.6 Naming schemes of Intel’s servers
Notes: 28

## Slide 29: 1.6 Naming schemes of Intel’s servers (1)
1.6 Naming schemes of Intel’s server processors
Until 2005 Intel made use of a naming scheme identifying clock frequency and server
configuration, like Xeon 2.8 GHz DP or Xeon 2.0 GHz MP, since it was advantageous for Intel as
their IC technology was superior to their competitors and provided higher clock frequencies.
a) Intel's server naming scheme until 2005
Remark
At that time AMD had their own IC fabrication with a less advanced IC technology,
so AMD's processors had lower clock frequencies.
To hide this deficiency, AMD introduced a new model naming scheme at the introduction
of their Athlon XP desktop line in 2003.
The new naming scheme consisted of a four digit number and the +character., e.g.
Athlon 1600+.
This designation reflected a relative performance level related to a given AMD DT model
(Athlon 1.4 GHz).
The relative performance was calculated from the average of a wide range of benchmarks.
The actual clock frequencies were lower figures, e.g. the Athlon XP 1600+ has a clock
frequency of 1.4 GHz.

## Slide 30: 1.6 Naming schemes of Intel’s servers (1)
.
In the first years of the 2000's clock frequencies became stagnating, as indicated below [168].
b) Intel's server naming scheme used between 2005 and 2011
Figure: Historical growth of clock rates [168]

## Slide 31: 1.6 Naming schemes of Intel’s servers (1b)
9000 series
Intel’s naming scheme of server processors, introduced in 2005
3000 series
5000 series
UP server
lines
Itanium lines
of processors
7000 series
MP server (4S)
lines
DP server (2S)
lines
Accordingly, Intel’s subsequent MP (4S) server processor lines were designated as follows:
Line | Processor | Based on | Intro
7000 | Paxville MP | Pentium 4 Prescott MP | 2005
7100 | Tulsa | Pentium 4 Prescott MP | 2006
7200 | Tigerton DC | Core 2 | 2007
7300 | Tigerton QC | Core 2 | 2007
7400 | Dunnington | Penryn | 2008
7500 | Beckton | Nehalem | 2010
.
As an aftermath Intel Intel could not continue to use its previous naming scheme and
introduced an AMD like naming scheme in 2005, as follows:
b) Intel's server naming scheme used between 2005 and 2011 -2

## Slide 32: 1.6 Naming schemes of Intel’s servers (2)
Product line: E3, E5 or E7 (E: Enterprise).
Wayness: How many processors are natively supported in a system
Socket type: Signifies processor performance,
Westmere/Sandy Bridge (without version number)
v2: Ivy Bridge
v3: Haswell
v4: Broadwell
c) Intel's renewed server naming scheme, introduced along with the Westmere line -1
In 4/2011 Intel renewed its entire naming scheme to reflect more details in the designations.
This resulted in the following new naming scheme for servers:
8: high performance
6: effective performance
4: entry level
Processor SKU: Last two digits of the model number
Figure: Intel’s new Xeon naming scheme [127]
Version: Common version number share a common microarchitecture
*

## Slide 33: 1.6 Naming schemes of Intel’s servers (3)
Remarks
1) The designation of the server generations v2, v3 etc. does not coincides with the designation
of the microarchitecture generations, as follows:
Microarchitecture | Architecture generation | Server generation
Westmere |  | (without designation) only E7
Sandy Bridge | Gen. 2 | (without designation) only E3/E5
Ivy Bridge | Gen. 3 | v2
Haswell | Gen. 4 | v3
Broadwell | Gen. 5 | v4
2) The Itanium line has not been renamed, it remained the 9000-line, with model numbers
of 9300, 9500, up to 9700

## Slide 34: 1.6 Naming schemes of Intel’s servers (4b)
High-end server lines | Models | Scalability | Core count up to | Socket | Intro
Westmere-EX | E7-2800 E7-4800 E7-8800 | 2-socket 4-socket 8-socket | 10C | LGA 1567 | 2011
Ivy Bridge-EX | E7-28xx v2 E7-48xx v2 E7-88xx v2 | 2-socket 4-socket 8-socket | 15C | LGA 2011-1 | 2014
Haswell-EX | E7-48xx v3 E7-88xx v3 | 4-socket 8-socket | 14C 18C | LGA 2011-1 | 2015
Broadwell-EX | E7-48xx v4 E7-88xx v4 | 4-socket 8-socket | 16C 22C | LGA 2011-1 | 2016
Intel's renewed naming scheme of servers introduced along with the Westmere line -3
Intel's designation for their EX lines became as follows:

## Slide 35: 1.6 Naming schemes of Intel’s servers (5)
Haswell
(LGA1150)
Mobiles and desktops
Haswell-E
(LGA2011)
High end desktops
(HEDs)
The Haswell family
Haswell-EP
(LGA2011)
Efficient performance servers, workstations
Haswell-EX
(LG2011)
High-end servers
Servers
Microservers
E3-1275L/1265L v3, 4C+G, HT, 6/2013 and 5/2014
E3-1240L/1230L/1220L v3, 2C/4C, HT, 6/2013 and 5/2014
UP Servers
E3-12x5/12x6 v3, 4C+G, HT, 6/2013 and 5/2014
E3-12x0/12x1 v3, 4C, HT, 6/2013 and 5/2014
E5-16xx v3, 4/6/8C, 9/2014
Workstations
2S-Servers
4S/8S-Servers
E5-26xx v3, 4/6/8/10/12/14/16/18C, 9/2014
E5-46xx v3, 6/10/12/14/16/18C, 6/2015
E7-48xx v3, 8/10/12/14C, 5/2015
E7-88xx v3, 4/10/16/18C, 5/2015
Example: Server product lines of the Haswell family
Haswell-EN
(LGA1150)
Microservers/
UP servers
Up to 18 cores
E7 designation
Up to 18 cores
E5 designation
Up to 8 cores
i7 designation
Up to 4 cores
i3/i5/i7 designations
Up to 4 cores
E3 designation
E5-24xx v3, 4/6/8/10C, 1/2015

## Slide 36: 1.6 Naming schemes of Intel’s servers (6)
Drawback of the implementation of Intel's - Westmere to Broadwell based
- 2S/4S/8S servers
There is a large number of different implementation alternatives of Intel's Westmere to Broadwell
based 2S to 8S server processors, as the next Figure demonstrates it.
*

## Slide 37: 1.6 Naming schemes of Intel’s servers (7)
Example: E5/E7 platform options built up of Ivy Bridge based server processors -1 [117]
Brickland platform: High-end (EX) platform options
E
Romley platform
EN: Entry level
EP: Efficient Performance level options

## Slide 38: 1.6 Naming schemes of Intel’s servers (8)
Example: E5/E7 processor features of Intel's Ivy Bridge based server processors -2 [117]
The main differences are between implementing the E5-EN, E5-EP and E7-EX Ivy Bridge
based server processors, as follows
 | E5-EN lines | E5- EP lines | E7-EX lines
Type of memory attachment to the on-die MC(s) | Directly attached DDR3 memory channels to a single or dual MCs |  | Attachment via 4 low line count proprietary 64-bit parallel channels (SMI2 channels) with on-board memory buffers, while 2 DDR3/4 channels are connected to each mem. buffer
No. of DDR3 memory channels | 3 DDR3 channels | 4 DDR3 channels | 8 DDR3 channels
No. of QPI links | 1 QPI link | 2 QPI links | 3 QPI links
No. of PCIe lanes | 3x8 lanes | 5x8 lanes | 4x8 lanes
PCH | 2S options: C600 (Patsburg) 4S options: C610 (Wellsburg) |  | C602 J (Patsburg J)

## Slide 39: 1.6 Naming schemes of Intel’s servers (9)
d) Latest naming scheme introduced along with the Skylake-SP processor line in 2017:
It aims at
introducing 4 performance grades instead of two (E7/E5) and
unifying the processor implementations of the 2S, 4S, 8S configurations,
as indicated in the following figures.
*

## Slide 40: 1.6 Naming schemes of Intel’s servers (10)
Unifying the implementation of the E7 and E5 series based on the Sjylake-SP [139]
(4S)
(-SP)
(4S/8S)
Haswell
Broadwell

## Slide 41: 1.6 Naming schemes of Intel’s servers (11)
Unifying the processor implementation of the 2S to 8S configurations [139]
LBG: Lewisburg (PCH)
OP: OmniPath

## Slide 42: 1.6 Naming schemes of Intel’s servers (12)
Corresponding new model numbering starting with the Skylake-SP processor line [140]
(OmniPath)
*

## Slide 43
1.7 Overview of Intel’s high-end server platforms
with multicore processors
Notes: 43

## Slide 44: 1.7 Overview of Intel’s high-end server platforms (1)
1.7 Overview of Intel’s high-end server platforms with multicore processors -1
Truland
(2005)
(90/65 nm)
Intel’s high-end server platforms built up of multicore processors
Brickland-EX
(2014)
(22/14 nm)
Boxboro-EX
(2010)
(45/32 nm)
Caneland
(2007)
(65/45 nm)
Purley
(2017)
(14 nm)
Pentium 4 Xeon MP
based
Ivy Bridge-EX/
Haswell-EX
Broadwell-EX
based
Nehalem-EX/
Westmere-EX
based
Core 2 Xeon MP
based
Skylake-SP
based
*

## Slide 45
Platform | Core | Techn. | Intro. | High-end server processor lines | Core count | Chipset | Proc. socket
Truland MP | Pentium 4 MP Prescott | 90 nm | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 1C | E8500 + ICH5 | LGA 604
 | Pentium 4 Presc. | 90 nm | 11/2005 | 7000 (Paxville MP) | 2x1C | E8501 + ICH5 | 
 | Pentium 4 Presc. | 65 nm | 8/2006 | 7100 (Tulsa) | 2x1C |  | 
Caneland MP | Core2 | 65 nm | 9/2007 | 7200 (Tigerton DC) 7300 (Tigerton QC) | 2C 2x2C | E7300 (Clarksboro)+ 631x/632x ESB | LGA 604
 | Penryn | 45 nm | 9/2008 | 7400 (Dunnington) | 6C |  | 
Boxboro-EX | Nehalem | 45 nm | 3/2010 | 7500 (Beckton/ Nehalem-EX) | 8C | 7500 (Boxboro) + ICH10 | LGA 1567
 | Westmere | 32 nm | 4/2011 | E7-4800 (Westmere-EX) | 10C |  | 
 | Sandy Bidge | 32 nm |  |  |  |  | 
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-4800 v2 (Ivy Bridge-EX) | 15C | C602J (Patsburg J) | LGA 2011-1
 | Haswell | 22 nm | 5/2015 | E7-4800 v3 (Haswell-EX) | 14C |  | 
 | Broadwell | 14 nm | 6/2016 | E7-4800 v4 (Broadwell-EX) | 16C |  | 
Purley | Skylake | 14 nm | 7/2017 | Platinum 8100 (Skylake-SP) | 28C | C620 (Lewisburg) | LGA 3647
Overview of Intel’s high-end 4S/8S platforms and processors
1.7 Overview of Intel’s high-end server platforms (2)

## Slide 46: 1.7 Overview of Intel’s high-end server platforms (3)
Remark: Intel’s transfer to 64-bit ISA in their server lines [97]
*

## Slide 47
2. Evolution of Intel’s high-end multicore
4S/8S server platforms
2.1 Overview of the evolution of key features
of high-end server platforms
2.2 The memory bandwidth bottleneck and its resolution
2.3 Overview of the evolution of high-end server platforms
Notes: 47

## Slide 48
2.1 Overview of the evolution of key features
of high-end server platforms
Notes: 48

## Slide 49: 2.1 Overview of the evolution of key features of high-end server platforms (1)
2.1 Overview of the evolution of key features of high-end server platforms
Intel's high-end multicore server processors had supported first 4-socket (4S or MP) and
later 8-socket (8S) platforms, as indicated in the Table below.
Platform | Core | Techn. | Intro. | High-end 4S/8S server processor lines | Core count | Scalability
Truland MP | Pentium 4 MP Prescott | 90 nm | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 1C | 4-socket servers (4S)
 | Pentium 4 Presc. | 90 nm | 11/2005 | 7000 (Paxville MP) | 2x1C | 
 | Pentium 4 Presc. | 65 nm | 8/2006 | 7100 (Tulsa) | 2x1C | 
Caneland | Core2 | 65 nm | 9/2007 | 7200 (Tigerton DC) 7300 (Tigerton QC) | 2C 2x2C | 4-socket servers (4S)
 | Penryn | 45 nm | 9/2008 | 7400 (Dunnington) | 6C | 
Boxboro-EX | Nehalem | 45 nm | 3/2010 | 7500 (Beckton/ Nehalem-EX) | 8C | 8-socket servers (8S)
 | Westmere | 32 nm | 4/2011 | E7-8800 (Westmere-EX) | 10C | 
 | Sandy Bidge | 32 nm |  |  |  | 
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-8800 v2 (Ivy Bridge-EX) | 15C | 8-socket servers (8S)
 | Haswell | 22 nm | 5/2015 | E7-8800 v3 (Haswell-EX) | 18C | 
 | Broadwell | 14 nm | 6/2016 | E7-8800 v4 (Broadwell-EX) | 24C | 
Purley | Skylake | 14 nm | 7/2017 | Platinum 8100 (Skylake-SP) | 28C | 8-socket servers (8S)
Table:Intel’s high-end multicore server platforms and processors

## Slide 50
 | Core | Techn. | Intro. | High-end 4S/8S server processor lines | Core count | Chipset | Proc. socket
Truland MP | Pentium 4 MP Prescott | 90 nm | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 1C | E8500 + ICH5 | LGA 604
 | Pentium 4 Presc. | 90 nm | 11/2005 | 7000 (Paxville MP) | 2x1C | E8501 + ICH5 | 
 | Pentium 4 Presc. | 65 nm | 8/2006 | 7100 (Tulsa) | 2x1C |  | 
Caneland | Core2 | 65 nm | 9/2007 | 7200 (Tigerton DC) 7300 (Tigerton QC) | 2C 2x2C | E7300 (Clarksboro)+ 631x/632x ESB | LGA 604
 | Penryn | 45 nm | 9/2008 | 7400 (Dunnington) | 6C |  | 
Boxboro-EX | Nehalem | 45 nm | 3/2010 | 7500 (Beckton/ Nehalem-EX) | 8C | 7500 + ICH10 | LGA 1567
 | Westmere | 32 nm | 4/2011 | E7-8800 (Westmere-EX) | 10C |  | 
 | Sandy Bidge | 32 nm |  |  |  |  | 
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-8800 v2 (Ivy Bridge-EX) | 15C | C602J (Patsburg J) | LGA 2011-1
 | Haswell | 22 nm | 5/2015 | E7-8800 v3 (Haswell-EX) | 18C |  | 
 | Broadwell | 14 nm | 6/2016 | E7-8800 v4 (Broadwell-EX) | 24C |  | 
Purley | Skylake | 14 nm | 7/2017 | Platinum 8100 (Skylake-SP) | 28C | C620 (Lewisburg) | LGA 3647
a) Core counts in Intel's high-end multicore 4S/8S server processors -1
2.1 Overview of the evolution of key features of high-end server platforms (3)

## Slide 51: 2.1 Overview of the evolution of key features of high-end server platforms (4)
Core count
2006
2008
2010
2012
2014
2016
Year
7000
(90 nm)
7300
(65 nm)
7400
(45 nm)
Nehalem-EX
(45 nm)
Westmere-EX
(32 nm)
Ivy-Bridge-EX
(22 nm)
Broadwell-EX
(14 nm)
*
*
*
*
*
2
4
8
18
28
24
10
6
15
*
*
~2x/4 years
~2x/2 years
Emergence of
L3 caches
in the Core 2 line
*
*
Haswell-EX
(22 nm)
Skylake-SP
(14 nm)
*
7100
(65 nm
16 MB L3)
a) Core counts in Intel's high-end multicore 4S/8S server processors -2
*

## Slide 52: 2.1 Overview of the evolution of key features of high-end server platforms (5)
a1) In early high-end multicore 4S processors core counts doubled roughly biannually -1
*
Core count
2006
2008
2010
2012
2014
2016
Year
7000
(90 nm)
7300
(65 nm)
7400
(45 nm)
Nehalem-EX
(45 nm)
Westmere-EX
(32 nm)
Ivy-Bridge-EX
(22 nm)
Broadwell-EX
(14 nm)
*
*
*
*
*
2
4
8
18
28
24
10
6
15
*
*
~2x/4 years
~2x/2 years
Emergence of
L3 caches
in the Core 2 line
*
*
Haswell-EX
(22 nm)
Skylake-SP
(14 nm)
*
7100
(65 nm
16 MB L3)

## Slide 53: 2.1 Overview of the evolution of key features of high-end server platforms (5b)
Doubling core counts in early server processors is obvious, since developments of the IC
technology allowed to double transistor counts roughly every two years, consequently,
in L3 cache-less processors twice as many transistors became available in every new
technology node, which permitted to double core counts also roughly biannually.
Remark
In the Figure indicating the grows of core counts, the 7100 line don't fit to the
straight line describing the evolution of core counts in early L3 cache-less high-end servers.
*
a1) In early high-end multicore 4S processors core counts doubled roughly biannually -2

## Slide 54: 2.1 Overview of the evolution of key features of high-end server platforms (5c)
a1) In early high-end multicore 4S processors core counts doubled roughly biannually -1
*
Core count
2006
2008
2010
2012
2014
2016
Year
7000
(90 nm)
7300
(65 nm)
7400
(45 nm)
Nehalem-EX
(45 nm)
Westmere-EX
(32 nm)
Ivy-Bridge-EX
(22 nm)
Broadwell-EX
(14 nm)
*
*
*
*
*
2
4
8
18
28
24
10
6
15
*
*
~2x/4 years
~2x/2 years
Emergence of
L3 caches
in the Core 2 line
*
*
Haswell-EX
(22 nm)
Skylake-SP
(14 nm)
*
7100
(65 nm
16 MB L3)

## Slide 55: 2.1 Overview of the evolution of key features of high-end server platforms (5d)
Doubling core counts in early server processors is obvious, since developments of the IC
technology allowed to double transistor counts roughly every two years, consequently,
in L3 cache-less processors twice as many transistors became available in every new
technology node, which permitted to double core counts also roughly biannually.
Remark
In the Figure indicating the grows of core counts, the 7100 line don't fit to the
straight line describing the evolution of core counts in early L3 cache-less high-end servers.
*
a1) In early high-end multicore 4S processors core counts doubled roughly biannually -2
The reason is straightforward, this Pentium 4-based line - although manufactured on a smaller
feature size (65 nm technology) has already a large, 16 MB L3 cache that reduces the
silicon area available for the cores and thus limits the core count.

## Slide 56: 2.1 Overview of the evolution of key features of high-end server platforms (6)
a2) Slowing down the rate of rising core counts after L3 caches appeared in
in Intel's Core 2 based high-end multicore 4S/8S server processors -1
Core count
2006
2008
2010
2012
2014
2016
Year
7000
(90 nm)
7300
(65 nm)
7400
(45 nm)
Nehalem-EX
(45 nm)
Westmere-EX
(32 nm)
Ivy-Bridge-EX
(22 nm)
Broadwell-EX
(14 nm)
*
*
*
*
*
2
4
8
18
28
24
10
6
15
*
*
~2x/4 years
~2x/2 years
Emergence of
L3 caches
in the Core 2 line
*
*
Haswell-EX
(22 nm)
Skylake-SP
(14 nm)
*
7100
(65 nm
16 MB L3)
Figure: Core counts in Intel's high-end multicore 4S/8S server processors
*

## Slide 57
 | Core | Techn. | Intro. | High-end 4S/8S server processors | Core count | L3 MB | Chipset | Proc. socket
Truland MP | Pentium 4 MP Prescott | 90 nm | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 1C | 8 | E8500 + ICH5 | LGA 604
 |  | 90 nm | 11/2005 | 7000 (Paxville MP) | 2x1C | -- | E8501 + ICH5 | 
 |  | 65 nm | 8/2006 | 7100 (Tulsa) | 2x1C | 16 |  | 
Caneland | Core2 | 65 nm | 9/2007 | 7200 (Tigerton DC) 7300 (Tigerton QC) | 2C 2x2C | -- | E7300 (Clarksboro)+ 631x/632x ESB | LGA 604
 | Penryn | 45 nm | 9/2008 | 7400 (Dunnington) | 6C | 16 |  | 
Boxboro-EX | Nehalem | 45 nm | 3/2010 | 7500 (Beckton/ Nehalem-EX) | 8C | 8x3 | 7500 + ICH10 | LGA 1567
 | Westmere | 32 nm | 4/2011 | E7-8800 (Westmere-EX) | 10C | 10x3 |  | 
 | Sandy Bidge | 32 nm |  |  |  |  |  | 
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-8800 v2 (Ivy Bridge-EX) | 15C | 15x2.5 | C602J (Patsburg J) | LGA 2011-1
 | Haswell | 22 nm | 5/2015 | E7-8800 v3 (Haswell-EX) | 18C | 18x2.5 |  | 
 | Broadwell | 14 nm | 6/2016 | E7-8800 v4 (Broadwell-EX) | 24C | 24x2.5 |  | 
Purley | Skylake | 14 nm | 7/2017 | Platinum 8100 (Skylake-SP) | 28C | 28x2.5 | C620 (Lewisburg) | LGA 3647
2.1 Overview of the evolution of key features of high-end server platforms (7)
L3 caches in Intel's high-end multicore 4S/8S server processor lines

## Slide 58: 2.1 Overview of the evolution of key features of high-end server platforms (8)
Thermal
sensors
2 cores
2 cores
2 cores
4 MB LLC
4 MB LLC
4 MB LLC
4 MB LLC
3 MB MLC
3 MB MLC
3 MB MLC
Tags
Tags
Data pad
Address pad
Implementing on-die L3 caches first in the Penryn-based Xeon 7400 MP (2008) [96]
8 MB L3
3 MB L2/2 cores
In Intel's Core 2 based high-end processor line L3 caches appeared first in the Xeon 7400
(see subsequent Figure and Table),

## Slide 59: 2.1 Overview of the evolution of key features of high-end server platforms (9)
Model | Technology | Core count | L3 cache | Transistors (million) | Die area (mm2)
7300 | 65 nm | 2x2 | no L3 | 582 | 286
7400 | 45 nm | 6 | 16 MB | 1900 | 503
Nehalem-EX | 45 nm | 8 | 8x3 MB | 2300 | 513
Westmere-EX | 32 nm | 10 | 10x3 MB | 2600 | 512
Ivy Bridge-EX | 22 nm | 15 | 14x2.5 MB | 4310 | 541
Haswell-EX | 22 nm | 18 | 18x2.5 MB | 5700 | 662
Broadwell-EX | 14 nm | 24 | 24x2.5 MB | 7200 | 456
(Source: Intel’s data)
After L3 caches appeared in Intel's Core 2 based high-end server line, transistor counts has
vastly risen, e.g. from 582 million in the L3 cache-less Xeon 7300 already to 1.9 billion
transistors in the Xeon 7400 that provides already an L3 cache, as indicated in the Table below.
a2) Slowing down the rate of rising core counts after L3 caches appeared in
in Intel's Core 2 based high-end multicore 4S/8S server processors -2

## Slide 60: 2.1 Overview of the evolution of key features of high-end server platforms (10)
But mainly due to power and die size restrictions Intel couldn't raise the resulting very high
transistor counts and thus also core counts in the same rate as before, instead only in a
modest rate of about doubling transistor and thus core counts in every two technology
nodes, i.e. in about four years, as seen in the Table below and the above Figure.
Model | Technology | Date of introduction | Core count | L3 cache | Transistors (million) | Die area (mm2)
7300 | 65 nm | 9/2007 | 2x2 | no L3 | 582 | 286
7400 | 45 nm | 8/2008 | 6 | 16 MB | 1900 | 503
Nehalem-EX | 45 nm | 3/2010 | 8 | 8x3 MB | 2300 | 513
Westmere-EX | 32 nm | 4/2011 | 10 | 10x3 MB | 2600 | 512
Ivy Bridge-EX | 22 nm | 2/2014 | 15 | 14x2.5 MB | 4310 | 541
Haswell-EX | 22 nm | 5/2015 | 18 | 18x2.5 MB | 5700 | 662
Broadwell-EX | 14 nm | 6/2016 | 24 | 24x2.5 MB | 7200 | 456
Table: Transistor count and die area of high-end server processors (Source: Intel)
Recently, the nascent lengthening of the cadence of IC technology transitions also reduces
the dynamics of raising core counts.
a2) Slowing down the rate of rising core counts after L3 caches appeared in
in Intel's Core 2 based high-end multicore 4S/8S server processors -3
After the 6-core 7400 with 16 MB L3 appeared a further doubling of the core counts (and
the L3 size) approximately biannually would require to double the already vastly increased
transistor count of the Xeon 7400 of 1.9 billion transistors in every new technology node.
*

## Slide 61: 2.1 Overview of the evolution of key features of high-end server platforms (11)
Remark -1
There is an anomaly in respect to the Xeon 7400, since this processor lies on the line of
L3-less processors whose core count doubled approximately every two years (following
Moore's law) rather than on the line attributed to the processors including an L3 cache
and having a reduced slope.

## Slide 62: 2.1 Overview of the evolution of key features of high-end server platforms (11b)
Core count
2006
2008
2010
2012
2014
2016
Year
7000
(90 nm)
7300
(65 nm)
7400
(45 nm)
Nehalem-EX
(45 nm)
Westmere-EX
(32 nm)
Ivy-Bridge-EX
(22 nm)
Broadwell-EX
(14 nm)
*
*
*
*
*
2
4
8
18
28
24
10
6
15
*
*
~2x/4 years
~2x/2 years
Emergence of
L3 caches
in the Core 2 line
*
*
Haswell-EX
(22 nm)
Skylake-SP
(14 nm)
*
7100
(65 nm
16 MB L3)
a) Core counts in Intel's high-end multicore 4S/8S server processors -2

## Slide 63: 2.1 Overview of the evolution of key features of high-end server platforms (11c)
Remark -2
The reason for this anomaly is as follows.
Model | Technology | Date of introduction | Core count | L3 cache | Transistors (million) | Die area (mm2)
7300 | 65 nm | 9/2007 | 2x2 | no L3 | 582 | 286
7400 | 45 nm | 8/2008 | 6 | 16 MB | 1900 | 503
Nehalem-EX | 45 nm | 3/2010 | 8 | 8x3 MB | 2300 | 513
Westmere-EX | 32 nm | 4/2011 | 10 | 10x3 MB | 2600 | 512
Ivy Bridge-EX | 22 nm | 2/2014 | 15 | 14x2.5 MB | 4310 | 541
Haswell-EX | 22 nm | 5/2015 | 18 | 18x2.5 MB | 5700 | 662
Broadwell-EX | 14 nm | 6/2016 | 24 | 24x2.5 MB | 7200 | 456
Table: Transistor count and die area of high-end server processors (Source: Intel)
The previous high-end 4S Xeon 7300 server processor has 4 cores, was fabricated
by 65 nm technology, incorporated 582 million transistors and occupied 286 mm2 silicon
area, as the Table below shows.

## Slide 64: 2.1 Overview of the evolution of key features of high-end server platforms (12)
If the next generation 6-core Xeon 7400 would have linearly more transistors and became
implemented instead of 65 nm already by 45 nm technology, the die area needed would be
6/4 x 286 mm2 x 0.5 = 214 mm2.
Nevertheless, the 7400 was fabricated on a 503 mm2 die, large enough for 6 cores plus the
L3 cache that covers about 50 % of the silicon area.
Accordingly, the Xeon 7400 fits to the processors whose die area was not yet burdened by
the L3 cache.
Remark cont.
Model | Technology | Date of introduction | Core count | L3 cache | Transistors (million) | Die area (mm2)
7300 | 65 nm | 9/2007 | 2x2 | no L3 | 582 | 286
7400 | 45 nm | 8/2008 | 6 | 16 MB | 1900 | 503
Nehalem-EX | 45 nm | 3/2010 | 8 | 8x3 MB | 2300 | 513
Westmere-EX | 32 nm | 4/2011 | 10 | 10x3 MB | 2600 | 512
Ivy Bridge-EX | 22 nm | 2/2014 | 15 | 14x2.5 MB | 4310 | 541
Haswell-EX | 22 nm | 5/2015 | 18 | 18x2.5 MB | 5700 | 662
Broadwell-EX | 14 nm | 6/2016 | 24 | 24x2.5 MB | 7200 | 456
Table: Transistor count and die area of high-end server processors (Source: Intel)
Subsequently, the 8 core 45 nm Nehalem-EX has been implemented practically on the same
die area (actually on 513 mm2) as the 7400, so this processor fits already to those with
the reduced slope (doubling approximately every 4 years).

## Slide 65
b) Memory transfer rates in Intel’s DTs and high-end multicore 4S/8S servers-1
2.1 Overview of the evolution of key features of high-end server platforms (13)
*
Transfer rate (MT/s)
50
100
500
Year
03
05
01
02
04
06
07
08
1000
3000
200
2000
~ 2*/4 years
DDR2
533
DDR2
667
DDR2 800
DDR3
1600
09
11
2010
12
13
15
DDR3
1067
2000

14
*
DDR3
1333
DDR3/1866
*
DDR
333
~ 2*/8 years
DDR
266
x
x
x
x
*
DDR
400
DDR2
667
DDR3
1600
DDR3/4
1866
DDR
400
DDR3
1067
DTs
4S/8S
Emergence of
DDR3 memory
16
17
*
*
*
*
*
*
x
x
DDR4
1866
DDR4
2666
Emergence of
DDR4 memory
*
*
DDR4/2133
x
DDR4/2400
*

## Slide 66: 2.1 Overview of the evolution of key features of high-end server platforms (14)
As the Figure shows, in the course of evolution transfer rates of DDR2 memories doubled
roughly every four years, that is roughly half as fast as transfer rates of core counts
of high-end 4S/8S server processors..
b) Memory transfer rates in Intel’s high-end multicore 4S/8S server processors -2
*

## Slide 67
b) Memory transfer rates in Intel’s DTs and high-end multicore 4S/8S servers-3
2.1 Overview of the evolution of key features of high-end server platforms (15)
*
Transfer rate (MT/s)
50
100
500
Year
03
05
01
02
04
06
07
08
1000
3000
200
2000
~ 2*/4 years
DDR2
533
DDR2
667
DDR2 800
DDR3
1600
09
11
2010
12
13
15
DDR3
1067
2000

14
*
DDR3
1333
DDR3/1866
*
DDR
333
~ 2*/8 years
DDR
266
x
x
x
x
*
DDR
400
DDR2
667
DDR3
1600
DDR3/4
1866
DDR
400
DDR3
1067
DTs
4S/8S
Emergence of
DDR3 memory
16
17
*
*
*
*
*
*
x
x
DDR4
1866
DDR4
2666
Emergence of
DDR4 memory
*
*
DDR4/2133
x
DDR4/2400
*

## Slide 68: 2.1 Overview of the evolution of key features of high-end server platforms (16)
Moreover, after DDR3 memory emerged the growth rate of memory transfer rates
slowed down to doubling rougly every eight years due to the higher complexity of this
technology.
b) Memory transfer rates in Intel’s high-end multicore 4S/8S server processors -4
*

## Slide 69
2.2 The memory bandwidth bottleneck and its resolution
Notes: 69

## Slide 70: 2.2 The memory bandwidth bottleneck and its resolution (1)
a) The memory bottleneck
2.2 The memory bandwidth bottleneck and its resolution
BWM/core = nM ∗ w ∗ TM /nC
with nM: Number of memory channels
w: Width of a memory channel (8 byte)
TM: Transfer rate of the memory (e.g 2.4 GT/s)
nC: Core count
The per core memory bandwidth of a socket (BWM/core) amounts to
If in a processor family the per core memory bandwidth should be preserved over
generations the emerging memory bandwidth gap needs to be compensated
by appropriately raising the number of memory channels (nM) on the platform.
Here we assume that the width of the memory channels (w) remains unchanged.
*
In servers every core may run independently from each other, consequently,
twice as many cores need twice as much bandwidth.
In other words while processor generations evolve the
per core memory bandwidth should be preserved, in other words
the memory bandwidth needs to be linearly scaled with the core count.
In subsequent processor generations however, memory transfer rates (TM) rise slower
than core counts (nC) , consequently, the per core memory bandwidth decreases and
a memory bandwidth gap arises.

## Slide 71: 2.2 The memory bandwidth bottleneck and its resolution (2)
The number of memory channels (nM) needed for preserving the per core
memory bandwidth of an n-core high-end server
nC | nM
2 | 2.0
4 | 2.8
6 | 3.5
8 | 4.0
10 | 4.5
12 | 4.9
14 | 5.3
16 | 5.6
20 | 6.3
24 | 6.9
32 | 8.0
48 | 9.8
64 | 11.3
It can be shown that in case when core counts and memory transfer rates are rising as
discussed before, a high-end server with nC cores needs approximately nM = √2 ∗ √n
memory channels per socket for preserving the per core memory bandwidth related to
typical early single core implementations.
Table: The number of memory channels (nM) needed
per socket for preserving the per core memory bandwidth
of a high-end server with nC cores
Required memory channel numbers are shown in the Table below.
*

## Slide 72: 2.2 The memory bandwidth bottleneck and its resolution (3)
In order to preserve the per core memory bandwidth the number of memory channels
rose rapidly from 1 per socket to 8 per socket in Intel's high-end server platforms,
as shown in the next Table.
The number of memory channels (nM) provided in Intel's high-end server lines
*

## Slide 73
2.2 The memory bandwidth bottleneck and its resolution (3b)
No. and max. transfer rate of memory channels in Intel's high-end server lines
Platform | Platform topology | Date of intro. | Processor | Technology | Core count (up to) | No. and max. speed of memory channels/socket | Kind of connecting memory Socket
Truland MP | SMP w/dual FSBs | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 90 nm | 1C | 1x DDR2-400/socket | 4 serial channels (IMI) via MCH LGA 604
 |  | 11/2005 | Xeon 7000 (P4) (Paxville MP) | 90 nm | 2x1C |  | 
 |  | 8/2006 | Xeon 7100 (P4) (Tulsa) | 65 nm | 2C |  | 
Caneland | SMP w/Quad FSBs | 9/2007 | Xeon 7200 (Core 2) Tigerton DC | 65 nm | 2C | 1x DDR2-667/socket (FB-DIMM) | 4 serial FB-DIMM channels via MCH LGA 604
 |  | 9/2007 | Xeon 7300 (Core 2) Tigerton QC | 65 nm | 2x2C |  | 
 |  | 9/2008 | Xeon 7400 (Penryn) (Dunnington) | 45 nm | 6C |  | 
Boxboro-EX | NUMA, fully connected for 4S platforms, partially connected for 8S platforms | 3/2010 | Nehalem-EX (Xeon 7500/ (Beckton) | 45 nm | 8C | 8x DDR3-1067/socket | 4 serial channels (SMI) /socket LGA 1567
 |  | 4/2011 | Westmere-EX (E7-8800) | 32 nm | 10C |  | 
Brickland |  | 2/2014 | Ivy Bridge-EX (E7-8800 v2) | 22 nm | 15C | 8x DDR3-1600/socket | 4 parallel channels (SMI2)/socket LGA-2011-1
 |  | 5/2015 | Haswell-EX (E7-8800 v3) | 22 nm | 18C | 8x DDR4-1866/socket | 
 |  | 6/2016 | Broadwell-EX (E7-8800 v4) | 14 nm | 24C | 8x DDR4-1866/socket | 
Purley |  | 7/2017 | Skylake-SP (Platinum 8100) | 14 nm | 28C | 6x DDR4-2666/socket | 6 direct attached DDR4 channels/socket LGA-3647

## Slide 74: 2.2 The memory bandwidth bottleneck and its resolution (4)
b) Limitations regarding to the number of standard DRAM channels that can be connected
to the MCH
The number of feasible memory channels is however severely limited typically to two
when high speed memory (e.g. DDR2/3/4) is attached in the traditional way, that is
by parallel DRAM channels via the MCH.
*
Providing enough memory bandwidth is one of the key challenges in designing server
processor platforms since multicores emerged.
This challenge is especially hard in multiprocessors since then the total memory bandwidth
demand is the product of the per core memory bandwidth need multiplied by both the
core count and the processor count.

## Slide 75: 2.2 The memory bandwidth bottleneck and its resolution (5)
Intel’s first generation MP servers made use of an SMP (Symmetric Multiprocessor) topology
while using only a single FSB that connects all 4 single core processors to the MCH
(North Bridge), and provided only two memory channels, as shown below.
Figure: Pentium 4 MP aimed MP server platform for single core processors
Xeon MP1
SC
Xeon MP1
SC
FSB
Xeon MP1
SC
Xeon MP1
SC
ICH
NB
E.g. HI 1.5
HI 1.5 266 MB/s
E.g. DDR-200/266
E.g. 400 MT/s
Example: Connecting memory in a Pentium 4-based single core Xeon MP platform

## Slide 76: 2.2 The memory bandwidth bottleneck and its resolution (6)
Example for Intel’s early Pentium 4 based server MP [101]

## Slide 77: 2.2 The memory bandwidth bottleneck and its resolution (7)
If high speed (e.g. DDR2/3/4) DIMMs are connected via the MCH to a platform by standard
parallel memory buses, a large number of cupper traces are needed on the mainboard, e.g.
240 traces for DDR2/DDR3 DIMMs or 284 lines for DDR4 DIMMs, to connect the MCH to the
DIMM sockets, as shown in the next Figures.
Why the number of memory channels is typically limited to two on MCHs ? -1
*

## Slide 78: 2.2 The memory bandwidth bottleneck and its resolution (8)
All these DIMMs
are 8-byte wide.
Pin counts of SDRAM to
DDR4 DIMMs
SDRAM
(SDR)
DDR
DDR2
DDR3
168-pin
184-pin
240- pin
240-pin
DDR4
284-pin
2.1 Overview of the Truland MP platform (1)
Notes: 78

## Slide 79: 2.2 The memory bandwidth bottleneck and its resolution (9)
Example: PCB routing for DDR2 DIMMs (240 pins) [169]
Remark: It needs a 3-layer PCB.

## Slide 80: 2.2 The memory bandwidth bottleneck and its resolution (10)
For implementing more than two memory channels using the available restricted width
of the MCH smaller and denser cupper traces would be required on the mainboard.
This however, would cause higher ohmic resistance and coupling capacitance, which
would end up in longer rise and fall times, as indicated next.
Why the number of memory channels is typically limited to two on MCHs ? -2
*

## Slide 81: 2.2 The memory bandwidth bottleneck and its resolution (11)
For Vin = 1V:
Modeling the temporal behavior of raising the voltage on DIMM traces by a serial RC network
Remark
Figure: The circuit model and the related expression for Vc [135]

## Slide 82: 2.2 The memory bandwidth bottleneck and its resolution (12)
Vc
(Vin = 1 V)
Raising the voltage on a capacitor of a serial RC network that modelling DIMM traces
= R * C

## Slide 83: 2.2 The memory bandwidth bottleneck and its resolution (13)
Raising the voltage on a capacitor of a serial RC circuit that models DIMM traces
while τ is doubled
Vc
(Vin = 1 V)
= R * C

## Slide 84: 2.2 The memory bandwidth bottleneck and its resolution (14)
Longer rise and fall times, however would prevent maintaining the target memory transfer
rate.
As a consequence, using high speed (e.g. DDR2/3/4) memory and connecting memory
centrally to the MCH via the standard parallel memory interface limits the number of
memory channels more or less to two.
Why the number of memory channels is typically limited to two on MCHs ? -3
*

## Slide 85: 2.2 The memory bandwidth bottleneck and its resolution (15)
c) Approaches for raising the number of memory channels in servers
This point will be discussed while considering the basic design space of connecting
memory subsystems to server platforms.

## Slide 86: 2.2 The memory bandwidth bottleneck and its resolution (16)
Where to connect the memory subsystem
to the server platform
How to connect
DIMMs to the MCs
Connecting the memory subsystem to server platforms
Basic design space of connecting memory subsystems to servers
*

## Slide 87: 2.2 The memory bandwidth bottleneck and its resolution (17)
Where to connect the memory subsystem
to the server platform
Connecting memory
to the MCH (Memory Control Hub)
(yielding SMPs)
This is a central connection of the memory.
It causes severe bandwidth imitations
for multiprocessor configurations, like
MP configurations.
Memory
Processor
MCH
Processor
Figure: Options for the design aspect of Where to connect the memory subsystem
to the server platform
c1) Where to connect the memory subsystems to the server platforms
*

## Slide 88: 2.2 The memory bandwidth bottleneck and its resolution (18)
Core 2/Penryn based
Caneland MP server platform (for up to 6 C)
(2007)
ESI: Enterprise System Interface
(4 PCIe lanes, 0.25 GB/s per lane (like the DMI interface,
providing 1 GB/s transfer rate in each direction)
Example for connecting memory to the MCH: Intel's Core 2/Penryn-based high-end
4S server [138]
631xESB/ 632xESB
ESI
FB-DIMM
DDR2-533/667
Core2 (2C/4C)
Penryn (6C)
Core2 (2C/4C)
Penryn (6C)
Core2 (2C/4C)
Penryn (6C)
Core2 (2C/4C)
Penryn (6C)
FSB
(1066 MT/s)
Xeon 7200
(Tigerton DC) 1x2C
Xeon 7300
(Tigerton QC) 2x2C
Xeon 7400
(Dunnington 6C)
/
/
4 channels
up to
8 DIMMs
per channel

## Slide 89: 2.2 The memory bandwidth bottleneck and its resolution (17)
Where to connect the memory subsystem
to the server platform
Connecting memory
to the MCH (Memory Control Hub)
(yielding SMPs)
This is a central connection of the memory.
It causes severe bandwidth imitations
for multiprocessor configurations, like
MP configurations.
Memory
Processor
MCH
Processor
Figure: Options for the design aspect of "Where to connect the memory subsystem
to the server platform"
c1) Where to connect the memory subsystems to the server platforms
*
Connecting memory directly
to the processors
(yielding NUMAs)
This is a per processor connection of the memory.
It provides an inherent scaling
of the memory bandwidth with the processor count,
i.e. it allows to provide more memory channels
to a server platform.
MCH
Processor
Processor

## Slide 90
Example for connecting memory directly to the processors: Intel's Nehalem-based
DP server architecture [138]
2.2 The memory bandwidth bottleneck and its resolution (19)

## Slide 91: 2.2 The memory bandwidth bottleneck and its resolution (20)
Montecito (2C) (2006)
Opteron server lines (1C) (2003)
Opteron server lines (2C) 2005)
and all subsequent AMD lines
PA-8800 (2004)
PA-8900 (2005)
and all previous PA lines
Core 2 Duo line (2C) (2006)
and all preceding Intel lines
Core 2 Quad line (2x2C) (2006/2007)
Penryn line (2x2C) (2008)
Nehalem lines (4) (2008)
and all subsequent Intel lines
Tukwila (4C) (2010)
AMD’s K7 lines (1C)
(1999-2003)
UltraSPARC III (1C) (2001)
and all subsequent Sun lines
UltraSPARC II (1C) (~1997)
Connection point of memory
Connecting memory to the processor(s)
(NUMA)
Connecting memory to the MCH
(SMP)
Transition of connecting memory to the processor(s) in the course of processor evolution
POWER1 (RS/6000) (1990)
direct connection via external circuitry
since POWER5 (2C) (2005)
on-die integrated mem. controller

## Slide 92: 2.2 The memory bandwidth bottleneck and its resolution (21)
How to connect DIMMs to the MCs
Connecting DIMMs
via standard DRAM interfaces
directly to the MCs
DIMMs are connected to one or more memory controllers (MCs) directly by standard DRAM interfaces.
The number of memory channels is limited due to spatial and electrical constraints typically to
two or three.
Standard DRAM
interface
DIMMs
MC in
MCH or processor
c2) How to connect DIMMs to the MCs
Connecting DIMMs via low line count links and
memory buffers (MBs) to the MCs
DIMMs are connected to one or more
memory controllers (MCs) via low line count interfaces and interface converters, called memory buffers (MBs)
in order to connect more memory channels
than feasible by using standard DRAM memory interfaces.
MB
MB
Standard DRAM
interface
Low line count
interface
DIMMs
Figure:Alternatives for choosing the connection path between the MCs and the DIMMs
MC in
MCH or processor
Memory Buffers
(MBs)
2. Evolution of Intel’s high-end 4S/8S server platforms (24)
*

## Slide 93: 2.2 The memory bandwidth bottleneck and its resolution (22)
Note
Based on the above discussion there are two orthogonal options to raise the number
of memory channels:
Connecting memory directly to the processors
Connecting DIMMs via low line count links and memory buffers (MBs) to the MCs.
*

## Slide 94: 2.2 The memory bandwidth bottleneck and its resolution (24)
Using low-line-count parallel links to connect MBs to the MCs
Connecting DIMMs via low-line-count links and memory buffers (MBs) to the MCs
Intel's implementation is the SMI 2 interface.
The MBs are connected to the MCs via
64-bit parallel, bidirectional links
using single-ended voltage reference signals,
termed VMSE (Voltage Mode Single Ended) signals (comprising about 110 lines).
Used in Intel's
Brickland platform (2014/2015/2016)
for 15C/18C/24C
Connecting DIMMs via low line count links and memory buffers (MBs) to the MCs
Concerning this point there are two basic options, as detailed below:
Using low-line-count serial links to connect MBs to the MCs
It comprises about 70 lines (e.g. 240 for DDR2/3).
Figure: Example for differential signaling [170]
Used in Intel's
early 4S or 8S platforms (2005 - 2011)
for 2C to 10C
*
The MBs are connected to the MCs via two unidirectional,
Point-to-Point serial, packet based links
typically with differential signaling.
Drawback: Serial/Parallel conversion is required in the MBs,
this increases dissipation.
Benefit: No Serial/Parallel conversion is required
in the MBs.

## Slide 95: 2.2 The memory bandwidth bottleneck and its resolution (25)
Using low-line-count serial links for connecting MBs to the MCs
Using low-line-count serial links for connecting MBs to the MCs
Using on-DIMM MBs
(FB-DIMMs)
Using on-board MBs
(on mainboard/riser card)
For implementing this design decision there are two alternatives depending upon how the
MBs are implemented:
Intel's IMI (Independent Memory Interface)
Used to connect DDR2 memory
in the Pentium 4 based
Truland MP platform (2005/2006)
(for 1C/2x1C/2C)
Used to connect DDR3 memory
in the Nehalem-EX and Westmere-EX based
Boxboro-EX platform (2010/2011)
(for 8C/10C)
(as no DDR3 based FB-DIMM memoty
became available)
Intel's SMI (Scalable Memory Interface)
Examples
The MBs are placed as stand alone units
onto the mainboard or riser cards
and are connected via serial links
to the MCs.
*

## Slide 96: 2.2 The memory bandwidth bottleneck and its resolution (26)
Example 1: Connecting DIMMs via low-line-count serial links and on-board MBs to the MCs
in Intel’s Pentium 4 based Truland MP server platform (2005) [164]
4x IMI

## Slide 97: 2.2 The memory bandwidth bottleneck and its resolution (27)
DDR2
DIMMs
4 x Xeon DC
7000/7100
E8501 NB
ICH5R SB
2 x MB
(termed XMB)
2 x MB
(termed XMB)
Example 1: Connecting DIMMs via low-line-count serial links and on-board MBs to the MCs
in Supermicro's Pentium 4 based Truland MP server board (X6QT8) (2006) [165]
Supermicro Motherboards, X6QT8, User Manual,
https://www.supermicro.com/products/motherboard/Xeon7000/E8501/X6QT8.cfm

## Slide 98
Nehalem-EX 8C
Westmere-EX 10C
7500 IOH
QPI
QPI
QPI
QPI
QPI
QPI
QPI
QPI
SMB
SMB
Nehalem-EX: up to DDR3-1067
Westmere-EX: up to DDR3-1333
SMB
SMB
SMB
SMB
SMB
SMB
ICH10
ESI
SMI: Scalable Memory Interface
(Serial link between the
processor and the SMB)
(Differential signaling, ~25 lanes)
SMB: Scalable Memory Buffer
(Conversion between the serial SMI and the parallel DDR3 DIMM interfaces)
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI
links
2x4 SMI
links
Example 2: Connecting DDR3 DIMMs via low-line-count serial links and on-board MBs to
the MCs: Intel's Nehalem-EX/Westmere-EX based Boxboro-EX high-end 4S/8S server
platform (assuming a single IOH)
ME
ME: Management Engine
Xeon 7500
(Nehalem-EX)
(Becton) 8C
Xeon E7-8800
(Westmere-EX) 10C
Nehalem-EX 8C
Westmere-EX 10C
Nehalem-EX 8C
Westmere-EX 10C
Nehalem-EX 8C
Westmere-EX 10C
/
Nehalem-EX/Westmere-EX based Boxboro-EX high-end 4S/8S server platform (for up to 10 C)
(2010/2011)
2 DIMMs/memory channel
4 x QPI up to 6.4 GT/s
36
PCIe
2.0
2.2 The memory bandwidth bottleneck and its resolution (35)

## Slide 99: 2.2 The memory bandwidth bottleneck and its resolution (36)
Example 2: Westmere-EX-based 2S server board
connecting DDR3 DIMMs via low line count
serial links and on-board MBs to the MCs
(Supermicro's X10DBT) 2014) [167]

## Slide 100: 2.2 The memory bandwidth bottleneck and its resolution (25)
Using low-line-count serial links for connecting MBs to the MCs
Using low-line-count serial links for connecting MBs to the MCs
Using on-DIMM MBs
(FB-DIMMs)
Using on-board MBs
(on mainboard/riser card)
For implementing this design decision there are two alternatives depending upon how the
MBs are implemented:
Intel's IMI (Independent Memory Interface)
Used to connect DDR2 memory
in the Pentium 4 based
Truland MP platform (2005/2006)
(for 1C/2x1C/2C)
Used to connect DDR3 memory
in the Nehalem-EX and Westmere-EX based
Boxboro-EX platform (2010/2011)
(for 8C/10C)
(as no DDR3 based FB-DIMM memoty
became available)
Intel's SMI (Scalable Memory Interface)
Examples
The MBs are placed as stand alone units
onto the mainboard or riser cards
and are connected via serial links
to the MCs.
DDR2 based FB-DIMM interface
Used to connect DDR2 based FB-DIMM memory
in the Core 2 and Penryn based
Caneland platform (2007/2008)
(for 2C/2x2C/6C)
The MBs are placed directly
on the DIMMs in form of FB-DIMMs
and are connected via FB-DIMM interfaces
to the MCs
*

## Slide 101: 2.2 The memory bandwidth bottleneck and its resolution (28)
Example for connecting DIMMs via serial links and on-DIMM MBs (FB-DIMMs) to the
MCs [166]

## Slide 102: 2.2 The memory bandwidth bottleneck and its resolution (29)
A brief introduction to FB-DIMM memories
FB-DIMM memories were standardized and introduced in the 2006/2007 timeframe .
They supported DDR2 memories up to DDR2-667.
FB-DIMMs connect the MC and the DIMMs via low line count serial buses whereby the
memory buffers providing serial/parallel conversion to the DIMMs are placed onto the
DIMMs, as shown in the next Figure.
*

## Slide 103: 2.2 The memory bandwidth bottleneck and its resolution (30)
Figure: FB-DIMM memory architecture [102]
Layout of an FB-DIMM based memory subsystem -1 [102]

## Slide 104: 2.2 The memory bandwidth bottleneck and its resolution (31)
The standardized FB-DIMM technology supports a cascaded connection of up to 8 FB-DIMMs
to a memory controller by a packet based, bidirectional, point-to-point link.
The link make use of differential signaling and includes 14 read/10 write lanes, as indicated
in the next Figure.
Layout of an FB-DIMM based memory subsystem -2 [102]
*

## Slide 105
Principle of differential signaling [170]
2.2 The memory bandwidth bottleneck and its resolution (32)

## Slide 106: 2.2 The memory bandwidth bottleneck and its resolution (33)
Figure: FB-DIMM memory architecture [102]
Layout of an FB-DIMM based memory subsystem -3 [102]

## Slide 107: 2.2 The memory bandwidth bottleneck and its resolution (34)
The 14 inbound lanes carry data from the memory to the memory controller whereas the
10 outbound lanes transfer commands and data from the memory controller to the memory.
The transfer rate is 6 times the transfer rate of the memory, i.e. 6x667=4 MT/s over the
differential lines.
Data and commands, transferred in 12 cycles, from one frame, that is an inbound frame
includes 12x14=168 bit whereas an outbound frame has 12x10=120 bits.
For more information we refer to the literature, e.g. [103].
Layout of an FB-DIMM based memory subsystem -4 [103]
Remark
Thus, after the emergence of DDR3 memories Intel was forced to move back to custom
DDR3 DIMMs connected by serial links and on-board memory buffers to the MCs in their
subsequent Boxboro-EX platform.
higher dissipation due to the necessary serial/parallel conversions,
longer access times because of cascading DIMMs and
the resulting higher price.
FB-DIMMs have a number of inherent drawbacks, such as
As a consequence, there was a small demand for DDR2-based FBDIMM memories and
memory vendors were reluctant to develop DDR3-based FB-DIMMs.

## Slide 108: 2.2 The memory bandwidth bottleneck and its resolution (25)
Using low-line-count serial links for connecting MBs to the MCs
Using low-line-count serial links for connecting MBs to the MCs
Using on-DIMM MBs
(FB-DIMMs)
Using on-board MBs
(on mainboard/riser card)
For implementing this design decision there are two alternatives depending upon how the
MBs are implemented:
Intel's IMI (Independent Memory Interface)
Used to connect DDR2 memory
in the Pentium 4 based
Truland MP platform (2005/2006)
(for 1C/2x1C/2C)
Used to connect DDR3 memory
in the Nehalem-EX and Westmere-EX based
Boxboro-EX platform (2010/2011)
(for 8C/10C)
(as no DDR3 based FB-DIMM memoty
became available)
Intel's SMI (Scalable Memory Interface)
Examples
The MBs are placed as stand alone units
onto the mainboard or riser cards
and are connected via serial links
to the MCs.
DDR2 based FB-DIMM interface
Used to connect DDR2 based FB-DIMM memory
in the Core 2 and Penryn based
Caneland platform (2007/2008)
(for 2C/2x2C/6C)
The MBs are placed directly
on the DIMMs in form of FB-DIMMs
and are connected via FB-DIMM interfaces
to the MCs
*

## Slide 109: 2.2 The memory bandwidth bottleneck and its resolution (37)
Where to connect the memory subsystem to the server platform
Connecting memory
via the MCH
(SMPs)
Connecting memory
directly to the
processors
(NUMAs)
Connecting DIMMs
via standard DRAM interfaces
directly to the MCs
Using on-DIMM MBs
(FB-DIMMs)
Using on-board MBs
(on mainboard/riser cards)
Using low-line-count serial links
to connect MBs to the MCs
Using low-line-count parallel links
to connect MBs to the MCs)
How to connect DIMMs to the MCs
Connecting DIMMs via low-line-count links and
memory buffers (MBs) to the MCs
FB-DIMM interface in Intel's
Caneland (2007/08)
for 2C/2x2C/6C
Intel's SMI2 interface in
Brickland (2014/15/16)
for 15C/18C/24C
Intel's IMI interface in
Truland MP (2005/06)
for 1C/2x1C/2C
Intel's SMI interface in
Boxboro EX (2010/11)
for 8C/10C
Previous MP
platforms
for 1C
DDR4 interface
in Intel's Purley
(2017) for 28C
c3) Design space of connecting memory subsystems to platforms -1
*

## Slide 110: 2.2 The memory bandwidth bottleneck and its resolution (38)
How to connect the memory subsystem
to the server platform
Connecting memory
via the MCH
(SMPs)
Connecting memory
directly to the
processors
(NUMAs)
FB-DIMM interface in Intel's
Caneland (2007/08)
for 2C/2x2C/6C
Intel's SMI2 interface in
Brickland (2014/15/16)
for 15C/18C/24C
Intel's IMI interface in
Truland MP (2005/06)
for 1C/2x1C/2C
Intel's SMI interface in
Boxboro EX (2010/11)
for 8C/10C
Previous MP
platforms
for 1C
DDR4 interface
in Intel's Purley
(2017) for 28C
DDR4 interface in
IBM's POWER 9
(2017) for 24C
IBM's SMI interface in
POWER 4 to POWER 8
(2001-2014) for 2C to 12C
FB-DIMM interface in
IBM's POWER 6/7
(2007/10) for 2C/8C
DDR2/3/4 interface
in AMD's servers
(2003-2017)
Design space of connecting memory subsystems to platforms -2
Connecting DIMMs
via standard DRAM interfaces
directly to the MCs
Using on-DIMM MBs
(FB-DIMMs)
Using on-board MBs
(on mainboard/riser cards)
Using low-line-count serial links
to connect MBs to the MCs
Using low-line-count parallel links
to connect MBs to the MCs)
How to connect DIMMs to the MCs
Connecting DIMMs via low-line-count links and
memory buffers (MBs) to the MCs
*

## Slide 111: 2.2 The memory bandwidth bottleneck and its resolution (39)
d) The FSB bottleneck in SMP configurations
In early SMP configurations (e.g. in first Pentium 4 based single core (SC) Xeon based systems)
there is a single FSB that interconnects the four processors with the NB (Northbridge),
as seen.
Xeon MP1
SC
Xeon MP1
SC
FSB
Xeon MP1
SC
Xeon MP1
SC
ICH
NB
E.g. HI 1.5
HI 1.5 266 MB/s
E.g. DDR-200/266
Figure: Pentium 4 MP aimed MP server platform (for single core processors)
E.g. 400 MT/s
Bandwidth data on the Figure reveal that the FSB limits the overall memory bandwidth.
Up to 3.2 GB/s
Up to 2 x 8 x 0.266 = 4.26 GB/s
*

## Slide 112: 2.2 The memory bandwidth bottleneck and its resolution (40)
Obviously, in SMP configurations with higher core count and memory speeds, a single FSB
may severely limit memory bandwidth and thus performance.
This FSB caused bandwidth bottleneck may resolved by using more than one FSB, as indicated
in the subsequent Figures.
Resolving the FSB bottleneck in SMP configurations
*

## Slide 113
Xeon MP1
SC
Xeon MP1
SC
FSB (400 MT/s)
Xeon MP1
SC
Xeon MP1
SC
Preceding ICH
Preceding NBs
E.g. HI 1.5
HI 1.5 266 MB/s
E.g. DDR-200/266
90 nm Pentium 4 Prescott MP aimed
Truland MP server platform (for up to 2 C)
(2005)
Previous Pentium 4 MP aimed
MP server platform (for single core processors)
(2004 and before)
85001/8501
ICH5
XMB
XMB
DDR-266/333
DDR2-400
XMB
XMB
HI 1.5
DDR-266/333
DDR2-400
Resolving the FSB bottleneck by using dual FSBs in dual core 4S server platforms
2.2 The memory bandwidth bottleneck and its resolution (41)
FSB up to
(800 MT/s)
Xeon 7000
(Paxville MP) 2x1C
Xeon 7100
(Tulsa) 2C
Xeon MP
(Potomac) 1C
/
/
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
1The 8500 MCH support only667 MT/sFSB speeds and is used in
single core configurations whereas the 8501 supports already
800 MT/s and is used for dual core configurations

## Slide 114
85001/8501
ICH5
XMB
XMB
DDR-266/333
DDR2-400
FSB
(800 MT/s)
XMB
XMB
HI 1.5
DDR-266/333
DDR2-400
Xeon 7000
(Paxville MP) 2x1C
Xeon 7100
(Tulsa) 2C
Xeon MP
(Potomac) 1C
/
/
1 The E8500 MCH supports an FSB of 667 MT/s and consequently only the SC Xeon MP (Potomac)
90 nm Pentium 4 Prescott MP aimed
Truland MP server platform (for up to 2 C)
(2006)
Core 2 aimed
Caneland MP server platform (for up to 6 C)
(2007)
ESI: Enterprise System Interface
4 PCIe lanes, 0.25 GB/s per lane (like the DMI interface,
providing 1 GB/s transfer rate in each direction)
HI 1.5 (Hub Interface 1.5)
8 bit wide, 66 MHz clock, QDR,
266 MB/s peak transfer rate
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
631xESB/ 632xESB
ESI
FBDIMM
DDR2-533/667
2.2 The memory bandwidth bottleneck and its resolution (42)
Resolving the FSB bottleneck by using quad FSBs in up to 6 core 4S server platforms
Core2 (2C/4C)
Penryn (6C)
Core2 (2C/4C)
Penryn (6C)
Core2 (2C/4C)
Penryn (6C)
Core2 (2C/4C)
Penryn (6C)
FSB
(1066 MT/s)
Xeon 7200
(Tigerton DC) 1x2C
Xeon 7300
(Tigerton QC) 2x2C
Xeon 7400
(Dunnington 6C)
/
/
4 channels
up to
8 DIMMs
per channel
7300

## Slide 115
2.3 Overview of the evolution of high-end server platforms
Notes: 115

## Slide 116
Platform | Platform topology | Date of intro. | Processor | Techno- logy | Core count (up to) | No./kind of the links to mem. buffers | No. of mem. channels/ mem. buffer | No. /speed of mem. channels (up to)
Truland MP | SMP w/dual FSBs | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 90 nm | 1C | 4 serial low-line-count links (IMI) between the MCH and mem. buffers (XMBs) | 2 memory channels/ XMB | 2x DDR2-800/ socket
 |  | 11/2005 | Xeon 7000 (Paxville MP) | 90 nm | 2x1C |  |  | 
 |  | 8/2006 | Xeon 7100 (Tulsa) | 65 nm | 2C |  |  | 
Caneland | SMP w/Quad FSBs | 9/2007 | Xeon 7200 Tigerton DC (Core 2) | 65 nm | 2C | 4 serial low-line-count FB-DIMM links between the MCH and mem. buffers (AMBs) | 1 memory channel/ AMB | 1x DDR2-667/ socket
 |  | 9/2007 | Xeon 7300 Tigerton QC (Core 2) | 65 nm | 2x2C |  |  | 
 |  | 9/2008 | Xeon 7400 (Dunnington) (Penryn) | 45 nm | 6C |  |  | 
Boxboro-EX | NUMA fully connect. by QPI buses | 3/2010 | Nehalem-EX (Xeon 7500/ (Beckton) | 45 nm | 8C | 4 serial low-line-count links (SMI) per socket to 4 mem. channels (SMBs) | 2 memory channels/ SMB | 8x DDR3-1067/ socket
 |  | 4/2011 | Westmere-EX (E7-8800) | 32 nm | 10C |  |  | 
Brickland | NUMA fully connect. by QPI buses | 2/2014 | Ivy Bridge-EX (E7-8800 v2) | 22 nm | 15C | 4 parallel low-line-count links (SMI2) per socket to 4 mem. buffers (SMBs) | 2 memory channels/ SMB | 8x DDR3-1600 (IWB) / DDR4-1866 (HSW)/ socket
 |  | 5/2015 | Haswell-EX (E7-8800 v3) | 22 nm | 18C |  |  | 
 |  | ?? | Broadwell-EX | 14 nm | 24C |  |  | 
Purley | NUMA fully connect. by UPI buses | 7/2017 | Skylake-SP | 14 nm | 28C | 6 psrallel DDR4 channels per socket | Direct attached | 6x DDR4-2666 mem. speed
2.3 Overview of the evolution of connecting memory in high-end server platforms
2.3 Overview of the evolution of high-end server platforms (1)

## Slide 117
From single core to dual core high-end 4S server platforms
(called the Truland MP server platform) -1
2.3 Overview of the evolution of high-end server platforms (2)
*
Aim: Providing more memory channels per core by introducing low-line-count serial links
(interfaces) and memory buffers (placed onto the mainboard) between the
memory controller (implemented in the MCH) and the DIMMs.

## Slide 118
Xeon MP1
SC
Xeon MP1
SC
FSB
Xeon MP1
SC
Xeon MP1
SC
Preceding ICH
Preceding NBs
E.g. HI 1.5
HI 1.5 266 MB/s
E.g. DDR-200/266
85001/8501
ICH5
XMB
XMB
DDR-266/333
DDR2-400
FSB
XMB
XMB
HI 1.5
DDR-266/333
DDR2-400
Xeon 7000
(Paxville MP) 2x1C
Xeon 7100
(Tulsa) 2C
Xeon MP
(Potomac) 1C
/
/
90 nm Pentium 4 Prescott MP aimed
Truland MP server platform (for up to 2 C)
(2006)
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
1Previous Pentium 4 MP aimed
MP server platform (for single core processors)
(2004 and before)
Evolution of single core high-end 4S server platforms to dual core high-end 4S server platforms (called Truland MP server platform) -2
2.3 Overview of the evolution of high-end server platforms (3)
IMI
IMI
IMI (Independent Memory Interface): Low-line-count (70 signal lines) serial interface vs. DDR2 with 240 pins.
XMB: eXternal Memory Bridge
*

## Slide 119
b) From dual core to up to 6-core high-end 4S server platforms
(called the Caneland server platform) -1
2.3 Overview of the evolution of high-end server platforms (4)
Aims: a) Utilizing DDR2-based FB-DIMM memory with serial, low-line-count links to the
memory controller (which is implemented in the MCH) and on-DIMM memory buffers
in-order to simplify system design.
b) A further objective is to raise FSB bandwidth by providing 4 FSB channels to the
processors.
In fact, FB-DIMMs need only a fraction of the lines compared to standard DDR2 DIMMs,
thus significantly more memory channels (up to 6 channels) may be connected to the MCH
than in case of high-line-count DDR2 DIMMs.
Furthermore, due to the cascaded interconnection of the FB-DIMMs (with repeater
functionality), up to 8 DIMMs may be interconnected to a single DIMM channel instead of
two or three as typical for standard DDR2 memory channels.
This results in considerably higher memory bandwidth and memory size by reduced
mainboard complexity.
Based on these benefits Intel decided to use FB-DIMM-667 memory in their server platforms,
first in their DP platforms already in 2006 followed by the Caneland MP platform in 2007,
as discussed before.
*

## Slide 120
Core2 (2C/4C)
Penryn (6C)
Core2 (2C/4C)
Penryn (6C)
Core2 (2C/4C)
Penryn (6C)
Core2 (2C/4C)
Penryn (6C)
7300
631xESB/ 632xESB
85001/8501
ICH5
XMB
XMB
DDR-266/333
DDR2-400
FSB
XMB
XMB
ESI
FSB
HI 1.5
DDR-266/333
DDR2-400
FB-DIMM
DDR2-533/667
Xeon 7000
(Paxville MP) 2x1C
Xeon 7100
(Tulsa) 2C
Xeon MP
(Potomac) 1C
/
/
1 The E8500 MCH supports an FSB of 667 MT/s and consequently only the SC Xeon MP (Potomac)
Xeon 7200
(Tigerton DC) 1x2C
Xeon 7300
(Tigerton QC) 2x2C
Xeon 7400
(Dunnington 6C)
/
/
90 nm Pentium 4 Prescott MP aimed
Truland MP server platform (for up to 2 C)
(2006)
Core 2 aimed
Caneland MP server platform (for up to 6 C)
(2007)
ESI: Enterprise System Interface
4 PCIe lanes, 0.25 GB/s per lane (like the DMI interface,
providing 1 GB/s transfer rate in each direction)
HI 1.5 (Hub Interface 1.5)
8 bit wide, 66 MHz clock, QDR,
266 MB/s peak transfer rate
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
Pentium 4 Xeon MP 1C/2x1C
b) Evolution of dual core high-end 4S server platforms to up to 6 core high-end 4S
platforms (called Caneland server platform) -2
2.3 Overview of the evolution of high-end server platforms (5)
4 channels
up to
8 DIMMs
per channel
*

## Slide 121
2.3 Overview of the evolution of high-end server platforms (6)
c) Evolution to the up to 10-core Boxboro-EX 4S/8S high-end server platform
(targeting the Nehalem-EX/Westmere-EX processors) -1
Aims: a) Raising per socket memory bandwidth of the 4S/8S server by connecting memory
directly to the processors.
b) Replacing FB-DIMMs by custom DDR3 DIMMs which are connected via serial,
low-line count links and on-board memory buffers.
This became necessary since memory vendors were reluctant to develop DDR3-based
FB-DIMMs, thus Intel was forced to move back to custom DDR3 DIMMs and
on-board memory buffers in their subsequent Boxboro-EX platform.
higher dissipation due to the necessary serial/parallel conversions,
longer access times because of cascading DIMMs and
the resulting higher price.
The reason for cancellation DDR3-based FB-DIMM developments was the small
market share achieved by DDR2-bsed FB-DIMMs.
This was caused by the inherent drawbacks of FB-DIMM memories, such as

## Slide 122
Nehalem-EX 8C
Westmere-EX 10C
7500 IOH
QPI
QPI
QPI
QPI
QPI
QPI
QPI
QPI
SMB
SMB
Nehalem-EX: up to DDR3-1067
Westmere-EX: up to DDR3-1333
SMB
SMB
SMB
SMB
SMB
SMB
ICH10
ESI
SMI: Scalable Memory Interface
(Serial link between the
processor and the SMB)
(Differential signaling, ~25 lanes)
SMB: Scalable Memory Buffer
(Conversion between the serial SMI and the parallel DDR3 DIMM interfaces)
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI
channels
2x4 SMI
channels
ME
ME: Management Engine
Xeon 7500
(Nehalem-EX)
(Becton) 8C
Xeon E7-8800
(Westmere-EX) 10C
Nehalem-EX 8C
Westmere-EX 10C
Nehalem-EX 8C
Westmere-EX 10C
Nehalem-EX 8C
Westmere-EX 10C
/
Figure: The Nehalem-EX, Westmere-EX aimed Boxboro-EX MP server platform (for up to 10 C)
(2010/2011)
2 DIMMs/memory channel
4 x QPI up to 6.4 GT/s
36
PCIe
2.0
2.3 Overview of the evolution of high-end server platforms (7)
*
c) Evolution to the up to 10-core Boxboro-EX 4S/8S high-end server platform
(targeting the Nehalem-EX/Westmere-EX processors) -2

## Slide 123: 2.3 Overview of the evolution of high-end server platforms (8)
Implementing memory extension buffers MBs)
Implementing stand alone MBs
mounted on the mainboard or
on a riser card
Implementing MBs
immediately on the DIMM
(called FB-DIMMs)
Truland MP platform
(2005/2006)
Caneland platform
(2007/2008)
Boxboro-EX platform
(2010/2011)
Brickland platform
(2014/2015)
Figure: Intel’s implementation of memory extension buffers
Returning to the stand alone memory buffer implementation in the Boxboro-EX
high-end platform from using FB-DIMMs -2
*

## Slide 124: 2.3 Overview of the evolution of high-end server platforms (9)
d) Evolution to the up to 24-core Brickland 4S/8S high-end server platform
(targeting the Ivy Bridge-EX/Haswell-EX/Broadwell-EX processors) -1
Aims: a) Reducing power dissipation by eliminating serial/parallel conversions.
The previous Boxboro-EX platform made use of serial, packet based, differential links
(called SMI links) between the memory controllers and the memory buffers
that included about 70 signal lines.
In the subsequent Brickland platform Intel eliminated serial/parallel conversions and
thus reduced power dissipation by replacing serial links by proprietary parallel links,
called SMI2 links.
SMI 2 links provide 64-bit parallel, bidirectional communication using single-ended
voltage reference signals, called VMSE (Voltage Mode Single Ended) signaling.
SMI2 links require altogether about 110 signal lines, that is about 50 % more lines
than SMI.
b) Providing faster, PCIe 3.0 lanes and connecting PCIe 3.0 lanes directly to the processors.
*

## Slide 125: 2.3 Overview of the evolution of high-end server platforms (10)
ME: Management Engine
3 x QPI up to 8.0 GT/s
SMI2: Scalable Memory Interface 2
(Parallel 64 bit VMSE data link between
the processor and the SMB)
SMB: Scalable Memory Buffer
(C102/C104: Jordan Creek)
(Performs conversion between the
parallel SMI2 and the parallel
DDR3-DIMM interfaces)
C102: 2 DIMMs/channel
C104: 3 DIMMs/channel
Xeon E7-8800 v2 / E7-8800 v3 / E7-8800 v4
(Ivy Bridge-EX) / (Haswell-EX) (Broadwell-EX)
15C 18C 24C
C602J PCH
(Patsburg J)
QPI
1.1
QPI
1.1
QPI 1.1
QPI 1.1
QPI 1.1
QPI 1.1
DMI2
4xPCIe2
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI2
channels
2x4 SMI2
channels
ME
Ivy Bridge-EX 15C
Haswell-EX 18C
Broadwell-EX 24C
Ivy Bridge-EX 15C
Haswell-EX 18C
Broadwell-EX 24C
Ivy Bridge-EX 15C
Haswell-EX 18C
Broadwell-EX 24C
Ivy Bridge-EX 15C
Haswell-EX 18C
Broadwell-EX 24C
PCIe 3.0
32
PCIe 3.0
32
PCIe 3.0
32
PCIe 3.0
32
Up to DDR3-1600 in lockstep mode and
up to DDR3-1333 in independent channel mode
PCIe 3.0 (instead of PCIe 2
directly connected to the processors)
d) Evolution to the up to 24-core Brickland 4S/8S high-end server platform
(targeting the Ivy Bridge-EX/Haswell-EX/Broadwell-EX processors) -2

## Slide 126: 2.3 Overview of the evolution of high-end server platforms (11)
Benefits of connecting PCIe 3.0 lanes directly to the processors
Increasing the lane count from 36 to 4 x 32 = 128 lanes.
Reducing the bandwidth demand between the processor and the chipset.
to replace the high-bandwidth QPI link between the processor and the chipset
by a low-bandwidth link (DMI2 link), comprising of 4 PCIe 2.0 lanes,
to reduce the number of QPI links from 4 to 3 per processor and
to integrate both chipset parts into a single PCH (Peripheral Control Hub).
This allows
*

## Slide 127: 2.3 Overview of the evolution of high-end server platforms (12)
e) Evolution to the up to 28-core Purley high-end 2S/4S/8S server platform
targeting the Skylake-SP processors) -1
Aim: Reducing power consumption and simplifying system implementation by eliminating
interface conversions and related memory buffers by connecting DDR4 memory directly
to the processors.
This requires a large socket (76x56 mm) with a high number of contacts (3647).
*

## Slide 128: 2.3 Overview of the evolution of high-end server platforms (13)
C621? PCH
(Lewisburg)
UPI
UPI
UPI
UPI
UPI
UPI
DMI3
4xPCIe3
ME
PCIe 3.0
40
PCIe 3.0
40
PCIe 3.0
40
40
PCIe 3.0
Platinum 8100
(Skylake-SP)
28C
Skylake-SP 28C
Skylake-SP 28C
Skylake-SP 28C
Skylake-SP 28C
e) Evolution to the up to 28-core Purley high-end 2S/4S/8S server platform
targeting the Skylake-SP processors) -2
Directly connected up to
DDR4-2666 memory
(no conversions)
3 x UPI up to 10.4 GT/s
*

## Slide 129
Platform | 4S platform topology | Date of intro. | Processor | Techno- logy | Core count (up to) | L2 cache | L3 cache (up to)
Truland MP | SMP w/dual FSBs | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 90 nm | 1C | 1 MB | 8 MB
 |  | 11/2005 | Xeon 7000 (Paxville MP) | 90 nm | 2x1C | 2 MB/C | --
 |  | 8/2006 | Xeon 7100 (Tulsa) | 65 nm | 2C | 1 MB /C | 16 MB
Caneland | SMP w/Quad FSBs | 9/2007 | Xeon 7200 Tigerton DC (Core 2) | 65 nm | 2C | 4 MB/C | --
 |  | 9/2007 | Xeon 7300 Tigerton QC (Core 2) | 65 nm | 2x2C | 4 MB/C | ---
 |  | 9/2008 | Xeon 7400 (Dunnington) (Penryn) | 45 nm | 6C | 3 MB/C | 16 MB
Boxboro-EX | NUMA fully connect. by 3 QPI buses | 3/2010 | Nehalem-EX (Xeon 7500/ (Beckton) | 45 nm | 8C | ¼ MB/C | 8x3 MB
 |  | 4/2011 | Westmere-EX (E7-8800) | 32 nm | 10C | ¼ MB/C | 10x3 MB
Brickland | NUMA fully connect. by 3 QPI buses | 2/2014 | Ivy Bridge-EX (E7-8800 v2) | 22 nm | 15C | ¼ MB/C | 15x2.5 MB
 |  | 5/2015 | Haswell-EX (E7-8800 v3) | 22 nm | 18C | ¼ MB/C | 18x2.5 MB
 |  | 6/2016 | Broadwell-EX (E7-8800 v4) | 14 nm | 24C | ¼ MB/C | 24x2.5 MB
Purley | NUMA fully connect. by 3 UPI buses | 7/2017 | Skylake-SP (Platinum 8100) | 14 nm | 28C | 1 MB/C. | 28x1.375 MB
Intel’s high-end 4S/8S server platforms – Cache architectures
2.3 Overview of the evolution of high-end server platforms (14)

## Slide 130
Platform | 4S platform topology | Date of intro. | Processor | Techno- logy | Core count (up to) | FSB/QPI | IF to chipset | PCIe
Truland MP | SMP w/dual FSBs | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 90 nm | 1C | 2xFSB 667 MT/s | HI1.5 (266 MB/s bidirectional) | 28 x PCIe lanes on the MCH
 |  | 11/2005 | Xeon 7000 (Paxville MP) | 90 nm | 2x1C | 2xFSB 800 MT/s |  | 
 |  | 8/2006 | Xeon 7100 (Tulsa) | 65 nm | 2C |  |  | 
Caneland | SMP w/Quad FSBs | 9/2007 | Xeon 7200 Tigerton DC (Core 2) | 65 nm | 2C | 4xFSB 1066 MT/s | ESI x4 (4x PCIe lanes) (1GB/s per direction) | 28 x PCIe lanes on the MCH
 |  | 9/2007 | Xeon 7300 Tigerton QC (Core 2) | 65 nm | 2x2C |  |  | 
 |  | 9/2008 | Xeon 7400 (Dunnington) (Penryn) | 45 nm | 6C |  |  | 
Boxboro-EX | NUMA fully connect. by 3 QPI buses | 3/2010 | Nehalem-EX (Xeon 7500/ (Beckton) | 45 nm | 8C | 4xQPI 6.4 GT/s (3 for NUMA) | QPI (6.4 GB/s) | 36 x PCIe 2.0 lanes on the IOH
 |  | 4/2011 | Westmere-EX (E7-8800) | 32 nm | 10C |  |  | 
Brickland | NUMA fully connect. by 3 QPI buses | 2/2014 | Ivy Bridge-EX (E7-8800 v2) | 22 nm | 15C | 3xQPI 1.1 8 GT/s | DMI2 x4 (4xPCIe 2.0) (2 GB/s per direction) | 32 x PCIe 3.0 lanes on the proc.
 |  | 5/2015 | Haswell-EX (E7-8800 v3) | 22 nm | 18C | 3xQPI 1.1 9.6 GT/s |  | 
 |  | 6/2016 | Broadwell-EX (E7-8800 v4) | 22 nm | 24C | 3xQPI 1.1 9.6 GT/s |  | 
Purley | NUMA fully connect. by 3 UPI buses | 2017 | Skylake-EX | 14 nm | 28C | 3xUPI 10.4 GT/s | DMI3 x4 (4xPCIe 3.0) (~ 4GB/s/dir. | 48 x PCIe lanes on the proc.
Intel’s high-end 4S/8S server platforms – Connectivity
2.3 Overview of the evolution of high-end server platforms (15)

## Slide 131: 2.3 Overview of the evolution of high-end server platforms (16)
ILP (rel. to Xeon 7200)
ST perf. (rel. to Xeon 7200)
2006
2008
2010
2012
2014
2016
Year
Xeon 7200
(65 nm), 2C
Xeon 7400
(45 nm), 6C
Nehalem-EX
(45 nm), 8C
Westmere-EX
(32 nm), 10C
Ivy-Bridge-EX
(22 nm), 15C
Broadwell-EX
(14 nm), 24C
*
*
*
1.0
*
*
~2x/12 years
1.1
1.2
1.3
1.4
1.5
1.6
*
Haswell-EX
(22 nm), 18C
0.5
1.0
1.5
2.0
2.5
3.0
0.0
*
*
*
*
*
*
*
*
*
*
Single thread (ST)
perf. rel. to Xeon 7200
fmax (base)
GHz
0.9
0.8
*
*
*
*
*
fmax (base)
ILP rel. to Xeon 7200
1.0
1.1
1.2
1.3
1.4
1.5
1.6
0.9
0.8
Intel’s high-end 4S/8S server platforms – Performance features (Source of data: Intel)
*

## Slide 132: 2.3 Overview of the evolution of high-end server platforms (17)
Supply voltage and max. transfer rate (speed) of major DRAM types [136]
*

## Slide 133: 2.3 Overview of the evolution of high-end server platforms (18)
~ 2 x /6 y
Evolution of memory transfer speeds in Samsung's DDR memory chips [136]

## Slide 134
3. Example 1: The Brickland platform
3.1 Overview of the Brickland platform
3.3 The Ivy Bridge-EX (E7-8800 v2) 8S processor line
3.4 The Haswell-EX (E7-8800 v3) 8S processor line
3.5 The Broadwell-EX (E7-8800 v4) 8S processor line
3.2 Key innovations of the Brickland platform vs.
the previous Boxboro-EX platform
It won't be discussed.
Notes: 134

## Slide 135
3.1 Overview of the Brickland platform
Notes: 135

## Slide 136
Platform | Core | Techn. | Intro. | high-end 4S/8S server processor lines | Core count | Chipset | Proc. socket
Truland MP | Pentium 4 MP Prescott | 90 nm | 3/2005 | 90 nm Pentium 4 MP (Potomac) | 1C | E8500 + ICH5 | LGA 604
 | Pentium 4 Presc. | 90 nm | 11/2005 | 7000 (Paxville MP) | 2x1C | E8501 + ICH5 | 
 | Pentium 4 Presc. | 65 nm | 8/2006 | 7100 (Tulsa) | 2x1C |  | 
Caneland MP | Core2 | 65 nm | 9/2007 | 7200 (Tigerton DC) 7300 (Tigerton QC) | 2C 2x2C | E7300 (Clarksboro)+ 631x/632x ESB | LGA 604
 | Penryn | 45 nm | 9/2008 | 7400 (Dunnington) | 6C |  | 
Boxboro-EX | Nehalem | 45 nm | 3/2010 | 7500 (Beckton/ Nehalem-EX) | 8C | 7500 (Boxboro) + ICH10 | LGA 1567
 | Westmere | 32 nm | 4/2011 | E7-8800 (Westmere-EX) | 10C |  | 
 | Sandy Bidge | 32 nm |  |  |  |  | 
Brickland | Ivy Bridge | 22 nm | 2/2014 | E7-8800 v2 (Ivy Bridge-EX) | 15C | C602J (Patsburg J) | LGA 2011-1
 | Haswell | 22 nm | 5/2015 | E7-8800 v3 (Haswell-EX) | 18C |  | 
 | Broadwell | 14 nm | 6/2016 | E7-8800 v4 (Broadwell-EX) | 24C |  | 
Purley | Skylake | 14 nm | 7/2017 | Platinum 8100 (Skylake-SP) | 28C | C620 (Lewisburg) | LGA 3647
3.1 Overview of the Brickland platform
Overview of Intel’s high-end 4S/8S server platforms and processor lines
3.1 Overview of the Brickland platform (1)

## Slide 137: 3.1 Overview of the Brickland platform (2)
Xeon E7-8800 v2
Xeon
E7-8800 v3
5/2015
3/2012
C602J
(Ivy Bridge-EX)
(Ivytown) 15C
(Haswell-EX) 18C
Brickland
2/2014
(PatsburgJ)
Attached via x4 DMI2
22 nm/4310 mtrs/541 mm2
¼ MB L2/C
37.5 MB L3
3 QPI 1.1 links 8 GT/s
4 SMI2 links to 4 SMBs
2 mem. channels/SMB
up to 3 DIMMs/mem. channel
up to DDR3-1600 MT/s
6 TB (96x64 GB)
32 PCIe 3.0
LGA 2011-1
22 nm/5560 mtrs/661 mm2
¼ MB L2/C
35 MB L3
3 QPI 1.1 links 9.6 GT/s
4 SMI2 links to 4 SMBs
2 mem. channels/SMB
up to 3 DIMMs/mem. channel
up to DDR4-1866 MT/s
6 TB (96x64 GB)
32 PCIe 3.0
LGA 2011-1
Ivy Bridge-EX-based
22 nm
2/2014
Haswell-EX based
22 nm
Platform
Cores
PCH
The Brickland (8S) platform
Xeon
E7-8800 v4
6/2016
(Broadwell-EX) 24C
14 nm/7200 mtrs/456 mm2
¼ MB L2/C
40 MB L3
3 QPI 1.1 links 9.6 GT/s
4 SMI2 links to 4 SMBs
2 mem. channels/SMB
up to 3 DIMMs/mem. channel
up to DDR4-1866 MT/s
6 TB (96x64 GB)
32 PCIe 3.0
LGA 2011-1
Ivy Bridge-EX based
Haswell-EX based
Broadwell-EX based
Broadwell-EX based
14 nm

## Slide 138: 3.1 Overview of the Brickland platform (3)
Xeon E7-8800 v2
(Ivy Bridge-EX)
(Ivytown) 15C
C602J PCH
(Patsburg J)
QPI
1.1
QPI
1.1
QPI 1.1
QPI 1.1
QPI 1.1
QPI 1.1
DMI2
4xPCIe2
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI2
channels
2x4 SMI2
channels
ME
Ivy Bridge-EX 15C
Ivy Bridge-EX 15C
Ivy Bridge-EX 15C
Ivy Bridge-EX 15C
PCIe 3.0
32
PCIe 3.0
32
PCIe 3.0
32
PCIe 3.0
32
Xeon E7-8800 v3
(Haswell-EX)
14C
/
Basic system architecture of the high-end 4S/8S Brickland server platform
(assuming 2x3 DIMMs/SMB)
SMB: Scalable Memory Buffer
(Performs conversion between the
parallel SMI2 and the parallel
DIMM interfaces)
SMI2: Scalable Memory Interface 2
(Parallel 64 bit VMSE data link between
the processor and the SMB)
ME: Management Engine (Dedicated microprocessor to manage the server via a console or remotely)
Xeon E7-8800 v4
(Broadwell-EX)
16C
/

## Slide 139
3.2 Key innovations of the Brickland platform vs.
the previous Boxboro-EX platform
Notes: 139

## Slide 140: 3.2 Key innovations of the Brickland platform (1)
3.2 Key innovations of the Brickland platform vs. the previous Boxboro-EX platform
3.2.1 Connecting PCIe links direct to the processors rather than to the MCH
3.2.2 New memory buffer design

## Slide 141: 3.2.1 Connecting PCIe links direct to the processors rather than to the MCH (1)
3.2.1 Connecting PCIe links direct to the processors rather than to the MCH -1
3.2.1.1 Overview
36 lanes of PCIe 2.0
2 x QPI
Boxboro platform [106]
Brickland platform [114]

## Slide 142: 3.2.1 Connecting PCIe links direct to the processors rather than to the MCH (2)
Connecting PCIe links direct to the processors rather than to the MCH -2
It has two major implications, including
Raising the PCIe lane count provided by the Brickland platform (see Section 3.2.1.2)
Reducing the bandwidth needed between the processors and the chipset (see Section 3.2.1.3)

## Slide 143: 3.2.1 Connecting PCIe links direct to the processors rather than to the MCH (3)
As long as the Boxboro-EX platform provides 36 PCIe lanes, the Brickland platform affords
32 PCIe lanes per processor, i.e. 4 x 32 = 132 lanes in total for a 4S platform, as shown below.
3.2.1.2 Raising the PCIe lane count provided by the Brickland platform -1
36 lanes of PCIe 2.0
2 x QPI
Boxboro platform
Brickland platform
Figure: Connecting PCIe links direct to the processors rather than to the MCH

## Slide 144: 3.2.1 Connecting PCIe links direct to the processors rather than to the MCH (4)
3.2.1.2 Raising the PCIe lane count provided by the Brickland platform -2
If the PCI lanes are connected directly to the processors rather than to the MCH, the number of PCIe lanes supported by the platform will scale linearly with the number of processors.
Per lane PCIe bandwidth:
PCI 2.0: 500 MB/s
PCI 3.0: 984.6 MB/s
In addition, the Brickland platform provides faster PCIe 3.0 lanes instead of PCI 2.0 lanes
of the previous Boxboro platform.

## Slide 145: 3.2.1 Connecting PCIe links direct to the processors rather than to the MCH (5)
3.2.1.3 Reducing the bandwidth demand between the processors and the chipset
By relocating the PCIe links from the MCH to the processors, the bandwidth needed
between the chipset and the processors becomes significantly reduced, as follows;
In the preceding Boxboro platform the MCH provides 36 PCIe 2.0 lanes with a total
bandwidth of 36x0.5 GB/s = 18 GB/s per direction.
This gives rise for using a QPI 1.1 bus width the bandwidth of 16.0 GB/s per direction
between the MCH and the processors.
By contrast, in the Brickland platform the PCIe lanes are connected immediately to the
processors and there is no need for providing the associated bandwidth.
This has three consequences;
Interconnecting the processors and the PCH by a DMI2 (4x PCIe 2.0) link
Providing only three QPI links per processor
Implementing a single chip “chipset”,
as discussed next.

## Slide 146: 3.2.1 Connecting PCIe links direct to the processors rather than to the MCH (6)
Due to the reduced bandwidth demand of the chipset-processor interface, it suffices now
to interconnect the PCH with a single processor via a DMI2 interface consisting of 4 PCIe 2.0
lanes that provide a bandwidth of up to 4x0.5=2 GB/s, rather than using a QPI bus with
a bandwidth of 16.0 GB/s.
a) Interconnecting the processors and the PCH by a DMI2 (4x PCIe 2.0) interface
Figure: The Haswell-EX implementation of the Brickland platform [114]

## Slide 147: 3.2.1 Connecting PCIe links direct to the processors rather than to the MCH (7)
b) Providing only three QPI links per processor -1
As the Brickland platform does not need an extra QPI bus to interconnect the processor with
the PCH, it has only 3 QPI buses per processor rather than four compared to the previous
(Boxboro-EX) platform, as shown in the next Figure.
Figure: The Haswell-EX implementation of the Brickland platform [114]

## Slide 148: 3.2.1 Connecting PCIe links direct to the processors rather than to the MCH (8)
Providing only three QPI links per processor -2
In addition, the Brickland platform supports already QPI 1.1 buses with the following speeds:
Ivy Bridge-EX based Brickland platforms: up to 8.0 Gbps
Haswell-EX based Brickland platforms: up to 9.6 Gbps

## Slide 149: 3.2.1 Connecting PCIe links direct to the processors rather than to the MCH (9)
c) Implementing a single chip “chipset”
Inspired by the reduced functionality, the chipset is now implemented as a single chip solution
instead of using two chips, as in the previous Boxboro platform.
The single chip “chipset” is now designated as the PCH (Platform Controller Hub).
It is in particular the C602 J or Patsburg-J PCH, as shown below.
Figure: The Haswell-EX implementation of the Brickland platform [114]

## Slide 150: 3.2.2 New memory buffer design (1)
3.2.2 New memory buffer design
a) Redesigned, basically parallel MC-SMB interface, called SMI2 interface
b) Enhanced DRAM interface
It has two main components, as follows:

## Slide 151: 3.2.2 New memory buffer design (2)
a) Redesigned, basically parallel MC-SMB interface, called SMI2 interface -1
Scalable Memory Buffer
(SMB)
SMI2 data
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
SMI CMD
DDR3/4
interface
Scalable Memory Buffer
(SMB)
SMI In
DIMM
DIMM
DIMM
DIMM
SMI Out
DDR3
interface
Boxboro-EX platform
Brickland platform
SMI: Serial, packet based link with
differential signaling
Up to 6.4 Gbps
SMI 2: 64-bit parallel, bidirectional data link with
single-ended voltage reference signaling,
(VMSE (Voltage Mode single Ended) signaling)
Up to 3200 MT/s

## Slide 152: 3.2.2 New memory buffer design (3)
The SMI link of the Boxboro-EX platform was a serial, packet based, differential link
including about 70 signal lines.
By contrast, as far as the data transfer is concerned, with the SMI2 link Intel changed to
64-bit parallel, bidirectional communication using single-ended voltage reference signals,
called VMSE (Voltage Mode Single Ended) signaling.
SMI 2 requires altogether about 110 signal lines, that is about 50 % more lines than SMI.
The reason for changing from serial transfer to parallel transfer in case of the data lines is
presumably the fact, that in this case AD/DA converting of data becomes superfluous and
this results in reduced dissipation.
The SMI 2 interface is used in the Brickland platform and operates
in Ivy Town-EX based platforms at a speed of up to 2667 MT/s,
in Haswell-EX based platforms at a speed of up to 3200 MT/s and
in Broadwell-EX based platforms at a speed of up to 3200 MT/s.
a) Redesigned, basically parallel MC-SMB interface, called SMI2 interface -2

## Slide 153: 3.2.2 New memory buffer design (4)
b) Enhanced DRAM interface
Scalable Memory Buffer
(SMB)
SMI2 data
DIMM
DIMM
DIMM
DIMM
DIMM
DIMM
SMI CMD
DDR3/4
interface
Scalable Memory Buffer
(SMB)
SMI In
DIMM
DIMM
DIMM
DIMM
SMI Out
DDR3
interface
Boxboro-EX platform
Brickland platform
Up to DDR3-1333
Up to 2 DIMMs per memory channel
Up to DDR4-1866
Up to 3 DIMMs per memory channel

## Slide 154: 3.2.2 New memory buffer design (5)
Operation modes of the SMBs in the Brickland platform [113]
Operation modes of the SMBs
Lockstep mode
Independent channel mode
(aka Performance mode)
In lockstep mode the same command is sent
on both DRAM buses.
The read or write commands are issued
simultaneously to the referenced DIMMs,
and the SMB interleaves the data on the
In the independent channel mode commands
sent to both DRAM channels are independent
from each other.

## Slide 155: 3.2.2 New memory buffer design (6)
DRAM speeds of the Brickland platform
Feature | Ivy Bridge-EX based (E7-8800 v2) | Haswell-EX based (E7-8800 v3)
SMB | C102/C104 | C112/C114
DDR4 speed | n.a. | Perf. mode: up to 1600 MT/s Lockstep mode: up to 1866 MT/s
DDR3 speed | Perf. mode: up to 1333 MT/s Lockstep mode: up to 1600 MT/s | Perf. mode: up to 1600 MT/s Lockstep mode: up to 1600 MT/s

## Slide 156: 3.2.2 New memory buffer design (7)
E7-8800 v3 /E7-4800 v3 family
(18-Core), w/ QPI up to 9.6 GT/s
Haswell-EX
Example for a Haswell-EX based 4S Brickland platform [115]
The SMBs with the DIMMs are installed on extra cards to be inserted into the 8 SMI2 slots.

## Slide 157: 3.2.2 New memory buffer design (8)
The mainboard and two of the memory cards to be inserted into the SMI2 slots of the
platform shown in the previous Figure [115]
Memory cards
Mainboard

## Slide 158
3.3 The Ivy Bridge-EX (E7-8800 v2) 4S/8S processor line
Notes: 158

## Slide 159: 3.3 The Ivy Bridge-EX (E7-8800 v2) 4S/8S processor line (1)
Intel developed a single processor to cover all server market segments from 1S to 8S, called
the Ivytown processor.
3.3 The Ivy Bridge-EX (8800 v2) 4S/8S processor line [116]
It is manufactured on the 22 nm technology, includes up to 15 cores built up on 4.31 billion
transistors on a die of 541 mm2.
Ivytown processor versions have a TDP of 40 to 150 W and operate at frequencies ranging
from 1.4 to 3.8 GHz.
The Ivytown processor was launched along with the Romley 2S server platform in 9/2013
followed by the Brickland 4S/8S platform in 2/2014.

## Slide 160: 3.3 The Ivy Bridge-EX (E7-8800 v2) 4S/8S processor line (2)
Server platforms and processor segments covered by the Ivytown processor [117]
Entry level
E5 2400 1, 2 sockets
Performance level
E5 2600 1, 2, 4 sockets
High-performance level
E7 4800/8800 2, 4, 8 sockets
E5 platform: Romley
E7 platform: Brickland

## Slide 161: 3.3 The Ivy Bridge-EX (E7-8800 v2) 4S/8S processor line (3)
E5, E7 platform alternatives built up of Ivytown processors [117]
Romley Entry and Performance level platform alternatives
Brickland High performance platform alternatives

## Slide 162: 3.3 The Ivy Bridge-EX (E7-8800 v2) 4S/8S processor line (4)
Block diagram of the Ivy Town processor
PCU: Power Control Unit
TAP: Test Access Port
FUSE: Fuse block, to configure the die
i.e. to have various core and
cache sizes as well as
different frequency and TDP
levels
DRNG: Digital Random Number
Generator
IIO: Integrated I/O block
HA: Home Agent providing
memory coherency
MC: Memory Controller
VMSE: Voltage-Mode Single-Ended
Interface (actually the
SMB)
The processor consists of 3 slices, each with 5 cores and associated LLC segments, as seen below.
Figure: Block diagram of the Ivy Town processor [116]

## Slide 163: 3.3 The Ivy Bridge-EX (E7-8800 v2) 4S/8S processor line (5)
Layout of the ring interconnect bus used for dual slices (10 cores) [125]

## Slide 164: 3.3 The Ivy Bridge-EX (E7-8800 v2) 4S/8S processor line (6)
Layout of the ring interconnect bus used for three slices (15 cores) [125]
There are 3 virtual rings.
Multiplexers (MUXs) dynamically interconnect the rings, as shown below.
Clockwise outer ring
Counter-clockwise outer ring
Figure: Three-slice ring interconnect with three virtual rings interconnected by multiplexers [125]

## Slide 165: 3.3 The Ivy Bridge-EX (E7-8800 v2) 4S/8S processor line (7)
Implementing lower core variants through chopping [116]

## Slide 166: 3.3 The Ivy Bridge-EX (E7-8800 v2) 4S/8S processor line (8)
Lower core alternatives of the Ivytown processor achieved by chopping [116]
15 cores
10 cores
6 cores

## Slide 167: 3.3 The Ivy Bridge-EX (E7-8800 v2) 4S/8S processor line (9)
TDP vs. core frequency in different Ivytown processor alternatives [116]

## Slide 168
3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line
Notes: 168

## Slide 169: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (1)
3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line
Launched in 5/2015
22 nm, 5.7 billion transistors, 662 mm (for 14 to 18 cores)
Number of cores
18 cores for 8S processors
14 cores for 4S ones (in 08/2015) instead of 18 cores

## Slide 170: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (2)
Basic layout of an 18 core 8S Haswell-EX v3 (E7-8800) processor [118]

## Slide 171: 3.4 The Haswell-EX (E7-8800 v3) 48S processor line (3)
Feature | Ivy Bridge-EX (E7-8800 v2) | Haswell-EX (E7-8800 v3)
Cores | Up to 15 | Up to 18
LLC size (L3) | Up to 15x2.5 MB | Up to 18x2.5 MB
QPI | 3xQPI 1.1 Up to 8.0 GT/s in both dir. (16 GB/s per dir.) | 3xQPI 1.1 Up to 9.6 GT/s in both dir. (19.2 GB/s per dir.)
SMB | C102/C104 (Jordan Creek) C102: 2 DIMMs/SMB C103: 3 DIMMs/SMB | C112/C114 (Jordan Creek 2) C112: 2 DIMMs/SMB C113: 3 DIMMs/SMB
VMSE speed | Up to 2667 MT/s | Up to 3200 MT/s
DDR4 speed | n.a. | Perf. mode: up to 1600 MT/s Lockstep mode: up to 1866 MT/s
DDR3 speed | Perf. mode: up to 1333 MT/s Lockstep mode: up to 1600 MT/s | Perf. mode: up to 1600 MT/s Lockstep mode: up to 1600 MT/s
TSX | n.a. | Supported
Contrasting key features of the Ivy Bridge-EX and Haswell-EX processors -1 [114]

## Slide 172: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (4)
We note that the Haswell-EX processors support Intel’s Transactional Synchronization Extension
(TSX) that has been introduced with the Haswell core, but became disabled in the Haswell-EP
processors due to a bug.
Contrasting key features of the Ivy Bridge-EX and Haswell-EX processors -1 [114]

## Slide 173: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (5)
Transactional Synchronization Extension (TSX)
Intel’s TSX is basically an ISA extension and its implementation to allow hardware supported
transactional memory.
Transactional memory is an efficient synchronization mechanism in concurrent programming
used to effectively manage race conditions occurring when multiple threads access shared
data.

## Slide 174: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (6)
Addressing race conditions
Basically there are two mechanisms to address race conditions in multithreaded programs,
as indicated below:
Locks
Transactional memory (TM)
Basic mechanisms to address races in multithreaded programs
Pessimistic approach,
it intends to prevent possible conflicts
by enforcing serialization of transactions
through locks.
Optimistic approach,
it allows access conflicts to occur
but provides a checking and repair mechanism
for managing these conflicts, i.e.
it allows all threads to access shared data simultaneously
but after completing a transaction,
it will be checked whether a conflict arose,
if yes, the transaction will be rolled back and
then replayed if feasible else
executed while using locks.
The next Figure illustrates these synchronization mechanisms.

## Slide 175: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (7)
Illustration of lock based and transaction memory (TM) based thread synchronization
[126]
Conflict, to be
repaired

## Slide 176: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (8)
We note that in their POWER8 (2014) IBM also introduced hardware supported transactional
memory, called Hardware Transactional Memory (HTM).

## Slide 177: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (9)
Contrasting the layout of the Haswell-EX cores vs. the Ivy Bridge-EX cores [111]
Haswell-EX has four core slides with 3x4 + 6 = 18 cores rather than 3x5 cores in case of
the Ivy Bridge-EX (only 3x 4 = 12 cores indicated in the Figure below).
Figure: Contrasting the basic layout of the Haswell-EX (E7 v3) and Ivy Bridge-EX (E7 v2)
processors [111]
Note that the E7-V3 has only two ring buses interconnected by a pair of buffered switches.

## Slide 178: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (10)
More detailed layout of the Haswell-EX die [111]

## Slide 179: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (11)
Die micrograph of an 18-core Haswell-EX processor [111]
22 nm, 5.7 billion transistors, 662 mm2

## Slide 180: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (12)
Main features of 4S and 8S Haswell-EX processors [120]

## Slide 181: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (13)
Power management improvements in the Haswell-EP and Haswell-EX server lines
The related product families are: the Xeon E5-4600/2600/1600 and the Xeon E7-8800/4800
The introduced key power management improvements include first of all:
Per core P-states (PCPS) and
Uncore frequency scaling
We underline that the installed OS has to support the above features.

## Slide 182: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (14)
Per core P-states (PCPS) in the HSW-EP and Haswell-EX lines [129], [130]
In the Haswell-EP and -EX server lines Intel introduced individual P-state control instructed
by the OS.
This means that each core can operate independently at individual clock rate and ssociated
core voltage.
Previously, in the Ivy Bridge and preceding generations all cores run at the same frequency
and voltage.

## Slide 183: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (15)
Remark 1 - Estimated gain of using individual P-states -1
Subsequently, we cite a study investigating the possible gain of using individual voltage and
clock domains [131].
The assumed microarchitecture of the study is seen below.
Figure: Assumed microarchitecture in the cited
study (clock generation not indicated)
PMU: Power Management Unit
Based on sensed data it determines
individual clock and voltage values.
Note that due to the different clock rates
FIFO Buffers are needed between the cores
and the Interconnect for clock synchronization.
Clock synchronization adds latency to the
memory and cache transfers

## Slide 184: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (16)
Remark 1 - Estimated gain of using individual P-states -2
General assessment of using single and multiple voltage domains stated in the study [131]:
"The advantage of a single voltage domain is the capability of sharing the current among the cores; when some cores consume less current or are turned off, current can be directed to the other active cores. This advantage comes at the cost of tying all the voltage domains together, forcing the same operation voltage to all cores.
On the other hand, multiple voltage domains topology provides the ability to deliver individual voltages and frequencies according to an optimization algorithm. In particular, when a single thread workload is executed, the entire CMP power budget can be assigned to a single core, which can consume 16 times higher power than each individual cores when executing a
balanced workload on all 16 cores. While in both cases the total CMP power is the same, separate power domains require at least one of the 16 VRs to deliver 16 times higher power than its nominal working point. Such a requirement is not feasible. The present study evaluates VR designed to deliver 130%–250% of the rated CMP current."

## Slide 185: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (17)
Estimated gain vs a baseline platform that does not make use of DVFS [131]
1V1C: Single Voltage domain, single Clock domain
nVnC: Multiple Voltage domains, multiple Clock domains
1VnC: Single Voltage domain, multiple Clock domains
The headroom is understood as the capability of the voltage regulators to deliver up to 130 % or 150 % of the rated current (the current consumed at the min. Vcc
design point (the lowest P point).
The study has shown that for low thread counts, typical in DT and mobile platforms, the use
of multiple voltage and clock domains degrades performance due to clock synchronization
needed that adds latency to memory and cache transfers.
By contrast, in processors that support a large number of threads, as typical in servers,
multiple voltage and frequency domains may be benefitial assuming that voltage regulators
have a high enough power delivery capability.

## Slide 186: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (18)
Remark 2 -Principle of operation of the Per-core P-state (PCPS) power management (simplified) -1
Method and apparatus for per core performance states US 20140229750 A1 2012/2014
US patent application 20140229750 A1 (filed in 2012 and issued in 2014) reveals details
of the implementation [133].
The Figure below illustrates PCPS for an 18 core Haswell-EX processor when the cores
run a four different P-states.
Figure: Illustration of PCPS for an 18-core Haswell-EX processor if the cores run a four P-states [133]

## Slide 187: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (19)
According to the patent each core includes a set of 32-bit registers, one register for each
thread (Registers 212 to 214) plus an additional register (Register 218), as indicated
for two cores (Core i and Core n) below.
Figure: Per core implemented registers used for PCPS [133]
Remark 2 -Principle of operation of the Per-core P-state (PCPS) power management (simplified) -2

## Slide 188: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (20)
The per-thread available registers (Registers 212 to 214) provide a set of fields, detailed in
the patent.
The OS determines for each thread the requested P-state needed for executing the thread
at efficient performance (i.e. at the min. clock rate needed to execute the thread without
substantially lengthening its runtime. Note here that each thread is scheduled only for
in given time windows thus a higher clock rate would not substantially reduce its runtime).
Available core logic evaluates the per-thread requests, determines the highest performance
P-state needed for the core and writes this values into the additional register
(Register 218).
Finally, the requested P-state is communicated to the Central Power Control Unit (230) and
it sets the related individual voltage regulator and clock generator (PLL) belonging
to the core considered to obtain the requested P-state.
Remark 2 -Principle of operation of the Per-core P-state (PCPS) power management (simplified) -3

## Slide 189: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (21)
Uncore frequency scaling [132]
  With uncore frequency scaling the uncore voltage and frequency is independently controlled
  from the core's voltage and frequency settings.
  To achieve this the uncore needs to be implemented on a separate voltage and clock domain.
Benefit of uncore frequency scaling
For compute bound applications core frequency may be raised without needing
to increase uncore frequency and voltage or
for memory-bound applications uncore frequency may be raised without needing to
increase core frequency and voltage.
This allows to optimize performance by consuming less power.
Remark [132]
In Nehalem the cores were DVFS controlled whereas the uncore run at a fixed frequency
In the Sandy Bridge and Ivy Bridge cores and uncore were tight together
in Haswell each core and the uncore is treated separately.

## Slide 190: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (22)
P4-based Tulsa (2006)
Performance comparison of high-end 4S/8S server processors -1 [121]
(The test workload is: CPU 45 nm Design Rule Check Tool C 2006 Rev.)
Core 2 Tigerton QC (2007)
Penryn Dunnington (2008)
Nehalem-EX (2010)
Westmere-EX (2011)
Ivy Bridge-EX (2014)
Haswell-EX (2015)

## Slide 191: 3.4 The Haswell-EX (E7-8800 v3) 4S/8S processor line (23)
Performance comparison of Intel's high-end 4S/8S server processors -2 [121]
Note that with their high-end 4S/8S server processors Intel achieved a more than 10-fold
performance boost in 10 years.

## Slide 192
3.5 The Broadwell-EX (E7-8800 v4) 4S/8S processor line
Notes: 192

## Slide 193: 3.5 The Broadwell-EX (E7-8800 v4) 4S/8S processor line (1)
3.5 The Broadwell-EX (E7-8800 v4) 4S/8S processor line
Positioning the 14 nm Broadwell-EX line [112]
Broadwell-EX
Haswell-EX
Ivy Bridge-EX

## Slide 194: 3.5 The Broadwell-EX (E7-8800 v4) 4S/8S processor line (2)
Planned features of the Brickland platform and the Broadwell-EX processor line -1 [122]

## Slide 195: 3.5 The Broadwell-EX (E7-8800 v4) 4S/8S processor line (3)
Main features of the Broadwell-EX processor line -2 [122]
As seen in the above Table, the planned features – except of having 24 cores – are the same
as implemented in the Haswell-EX line.

## Slide 196: 3.5 The Broadwell-EX (E7-8800 v4) 4S/8S processor line (4)
Layout of the Broadwell-EX die [128]

## Slide 197: 3.5 The Broadwell-EX (E7-8800 v4) 4S/8S processor line (5)
4S Cluster on Die (COD) Mode [128]
COD is a performance enhancing feature, introduced with Haswell-EP, as 2S COD mode.
Broadwell-EX adds 4S COD capability by dividing 24 cores, 24 LLCs and the Home Agents
(HA) into two clusters, as seen below.
Figure: 4S Cluster on Die (COD) Mode [128]

## Slide 198: 3.5 The Broadwell-EX (E7-8800 v4) 4S/8S processor line (6)
Principle of operation [128]
Each LLC cluster operates as an independent caching agent.
OS creates NUMA domains such that most memory accesses remain within the cluster.
Benefits
LLC access latency is reduced as the cache slices are more localized to the cores.
Memory system latency is reduced because the number of threads seen by each
Home Agent is reduced and this increases the likelihood that memory requests hit
open pages in the memory controller.

## Slide 199: 3.5 The Broadwell-EX (E7-8800 v4) 4S/8S processor line (7)
Remark - Introduction of the COD mode already in Haswell-EP for 1S and 2S servers [134]
In case of an 18 core Haswell-EP (E5-2600 v3) processor the cores are partitioned into 2x 9 cores
as follows:
Figure: Partitioning 18 cores into 2x 9 cores for the COD mode in a Haswell-EP processor [134]

## Slide 200: 3.5 The Broadwell-EX (E7-8800 v4) 4S/8S processor line (8)
 | Cores / Threads | Clock / Turbo | L3 Cache | QPI | TDP | MSRP
Xeon E7-8890 v4 | 24 / 48 | 2.2 / 3.4 Ghz | 60 MB | 9.6 GT / s | 165 W | $7174.00
Xeon E7-8880 v4 | 22 / 44 | 2.2 / 3.3 Ghz | 55 MB | 9.6 GT / s | 150 W | $5895.00
Xeon E7-8870 v4 | 20 / 40 | 2.1 / 3.0 Ghz | 50 MB | 9.6 GT / s | 140 W | $4672.00
Xeon E7-8860 v4 | 18 / 36 | 2.2 / 3.2 Ghz | 45 MB | 9.6 GT / s | 140 W | $4061.00
Xeon E7-8855 v4 | 14 / 28 | 2.1 / 2.8 Ghz | 35 MB | 9.6 GT / s | 140 W | N/A
Xeon E7-8867 v4 | 18 / 36 | 2.4 / 3.3 Ghz | 45 MB | 9.6 GT / s | 165 W | $4672.00
Xeon E7-8891 v4 | 10 / 20 | 2.8 / 3.5 Ghz | 60 MB | 9.6 GT / s | 165 W | $6841.00
Xeon E7-8893 v4 | 4 / 8 | 3.2 / 3.5 Ghz | 60 MB | 9.6 GT / s | 140 W | $6841.00
Xeon E7-4850 v4 | 16 / 36 | 2.1 / 2.8 Ghz | 40 MB | 8.0 GT / s | 115 W | $3003.00
Xeon E7-4830 v4 | 14 / 28 | 2.0 / 2.8 Ghz | 35 MB | 8.0 GT / s | 115 W | $2170.00
Xeon E7-4820 v4 | 10 / 20 | 2.0 Ghz | 25 MB | 6.4 GT / s | 115 W | $1502.00
Xeon E7-4809 v4 | 8 / 16 | 2.1 Ghz | 20 MB | 6.4 GT / s | 115 W | $1223.00
Main features of the Broadwell-EX (Xeon E7-8800 v4 and 4800 v4) lines [128]

## Slide 201
4. Example 2: The Purley platform
4.1 Overview of the Purley platform
4.3 The Skylake-SP (Xeon x100) 2S/4S/8S processor line
4.2 Key innovations of the Purley platform vs.
the previous Brickland platform
Notes: 201

## Slide 202
4.1 Overview of the Purley platform
Notes: 202

## Slide 203: 4.1 Overview of the Purley platform (1)
4.1 Overview of the Purley platform
The Purley platform is introduced in 7/2017, termed also as the Scalable platform.
It is based on the 14 nm Skylake-SP (Scalable Family Processor) server lines.
Designed to support existing and emerging server application domains, such as data center,
and network workloads including cloud computing, HPC and artificial intelligence.
*

## Slide 204: 4.1 Overview of the Purley platform (2)
Positioning of the Purley platform [112]
Broadwell-EX
Haswell-EX
Ivy Bridge-EX
Skylake-SP

## Slide 205: 4.1 Overview of the Purley platform (3)
Main features of the Purley platform based on the Skylake-SP processor line -1 [122]
8 /
(C602J)
DPC: DIMMs Per Channel

## Slide 206: 4.1 Overview of the Purley platform (4)
Drawback of the implementation of Intel's recent server lines
Large diversity of the recent server implementations, as indicated in the next slides.

## Slide 207: 4.1 Overview of the Purley platform (5)
Example: E5/E7 platform options built up of Ivy Bridge based server processors [117]
Romley platform: Entry and Efficient Performance level
platform options
(EN: 24xx v3, EP: 26xx v3, 46xx v3
Brickland platform: High-end (EX) platform options
E

## Slide 208: 4.1 Overview of the Purley platform (6)
Attaching memory to Intel's servers (from Nehalem to Broadwell based servers)
Direct attaching memory to EN/EP servers
Attaching memory to Intel's servers
Indirect attaching memory to EX servers
Attaching up to 4 standard DDR memory channels
directly to to processor die
Attaching 8 standard DDR memory channels via
4 low line count serial or proprietary 64-bit parallel
channels (SMI) with memory buffers, while
two standard DDR memory channels
can be connected to each memory buffer (SMB)
C602J PCH
(Patsburg J)
QPI
1.1
QPI
1.1
QPI 1.1
QPI 1.1
DMI2
4xPCIe2
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI2
channels
ME
Broadwell-EX
24C
Broadwell-EX
24C
PCIe 3.0
32
PCIe 3.0
32
Figure: Sandy Bridge-EP based server [142]
Figure: Part of a Broadwell-EX based server
*

## Slide 209: 4.1 Overview of the Purley platform (7)
Reducing the diversity of the implementation of Intel's server lines by the Skylake-SP
processor line in 2017:
It is achieved by
unifying the implementation of the E5 and E7 series and
unifying the processor implementations of the 2S, 4S and 8S configurations,
as indicated in the following figures.
*

## Slide 210: 4.1 Overview of the Purley platform (8)
Unifying the E7 and E5 processor series in the Purley 2S platform [139]
E7-4800 v4
E7-8800 v4
*

## Slide 211: 4.1 Overview of the Purley platform (9)
LBG: Lewisburg (PCH)
OP: OmniPath
Unifying the processor implementations of the 2S, 4S and 8S configurations [139]

## Slide 212: 4.1 Overview of the Purley platform (10)
New model numbering for the Skylake-SP processor line [140]
*

## Slide 213: 4.1 Overview of the Purley platform (11)
Main features of the Platinum, Gold, Silver and Bronze series [143]

## Slide 214: 4.1 Overview of the Purley platform (12)
Supported platform topologies - ranging from 2S to 8S [139]
LBG: Lewisburg (PCH)
OP: OmniPath

## Slide 215: 4.1 Overview of the Purley platform (13)
Example: 2S server Skylake-SP configuration [139]
TPM: Trusted Platform Module

## Slide 216: 4.1 Overview of the Purley platform (14)
Example: Mainboard of a 2S server based on Skylake-SP processors [144]

## Slide 217: 4.1 Overview of the Purley platform (15)
IPC improvement in Intel's Core 2 family (Core 2 to Skylake) [146]
*

## Slide 218: 4.1 Overview of the Purley platform (16)
Single-thread performance improvement in Intel's 2S servers [146]

## Slide 219: 4.1 Overview of the Purley platform (17)
Multi-thread integer performance (throughput) improvement in Intel's 2S server lines
[147]
*

## Slide 220: 4.1 Overview of the Purley platform (18)
Benchmark results published by Intel for running the Cinebench R35 benchmark [147]
8 cores
~450 $
28 cores
~8700 $

## Slide 221: 4.1 Overview of the Purley platform (19)
Benchmark result published by AMD for running molecular dynamics [148]

## Slide 222
4.2 The Skylake-SP (Xeon x100) 2S/4S/8S processor line
Notes: 222

## Slide 223
4.2.1 Overview
Notes: 223

## Slide 224: 4.2.1 Overview (1)
New model numbering for the Skylake-SP processor line [140]
*

## Slide 225: 4.2.1 Overview (2)
Up to 28 cores [139]

## Slide 226: 4.2.1 Overview (3)
Main features of the Skylake-SP Platinum, Gold, Silver and Bronze series [149]

## Slide 227: 4.2.1 Overview (4)
Up to four lineups in all four series (Platinum, Gold, Silver, Bronze) [146]
It consists of various engineering requirements deemed essential to the reliability, availability
and durability of equipment.
(NEBS compliant)
NEBS compliant [150]:
NEBS (Network Equipment Building System) is a standard originating from Bell.

## Slide 228: 4.2.1 Overview (5)
Main features of the introduced Skylake-SP models [146]

## Slide 229: 4.2.1 Overview (6)
Die configurations - XCC die (up to 28 cores) [139]

## Slide 230: 4.2.1 Overview (7)
Die configurations - HCC die (up to 18 cores) [139]

## Slide 231: 4.2.1 Overview (8)
Die configurations - LCC die (up to 10 cores) [139]

## Slide 232: 4.2.1 Overview (9)
The Skylake-SP XCC die (28 cores) [151]

## Slide 233: 4.2.1 Overview (10)
The Skylake-SP HCC die (18 cores) [152]

## Slide 234: 4.2.1 Overview (10b)
Expected die sizes [155]
Layout | Arrangement | Dimensions (mm) | Die Area (mm2)
LCC | 3x4 (10-core) | 22.0 x 14.0 | 308 mm2
HCC | 4x5 (18-core) | 22.0 x 21.5 | 473 mm2
XCC | 5x6 (28-core) | 21.5 x 31.5 | 677 mm2
Note
Intel does not give any more die are figures, above data are estimates from [155].

## Slide 235: 4.2.1 Overview (11)
High-level overview of the microarchitecture of a Skylake-SP core [139]

## Slide 236: 4.2.1 Overview (12)
Quantitative improvements of the Skylake-SP microarchitecture vs. the previous one [139]

## Slide 237
4.2.2 Key innovations of the Skylake-SP processor line - Overview
Notes: 237

## Slide 238: 4.2.2 Key innovations of the Skylake-SP processor line - Overview (1)
Broadwell-EX
Skylake-SP
Contrasting key features of the Broadwell-EX and the Skylake-SP processors [153], [139]
8 channels DDR3/4

## Slide 239: 4.2.2 Key innovations of the Skylake-SP processor line - Overview (2)
New Skylake-SP features [154]

## Slide 240: 4.2.2 Key innovations of the Skylake-SP processor line - Overview (3)
AVX512
Re-architected L2/L3 cache hierarchy
6 direct attached DDR4 memory channels
Mesh architecture
UPI (Ultra Path Interconnect)
In-package integrated OmniPath host fabric interface
New socket
Key innovations of the Skylake-SP processor line discussed
*

## Slide 241
a) AVX512
Notes: 241

## Slide 242: a) AVX512 (1)
Designation | Intro. | Processor line | Technology | SIMD registers | SIMD Register set | Instruction set
MMX | 1997 | Pentium MMX | 350 nm | MM [0:7]1 | 8x64 bit | FX SIMD
SSE | 1999 | Pentium III | 250 nm | XMM [0:7] | 8x128 bit | FX/FP SIMD
SSE2 | 2000 | Pentium 4 | 180 nm | XMM [0:15] | 16x128 bit | FX/FP SIMD
AVX | 2011 | Sandy Bridge | 32 nm | YMM [0:15] | 16x256 bit | FP SIMD
AVX2 | 2013 | Haswell | 22 nm | YMM [0:15] | 16x256 bit | FX/FP SIMD
AVX512 | 2017 | Skylake-SP | 14 nm | ZMM [0:31] | 32x512 bit | FX/FP SIMD
a) AVX512
Evolution of Intel's SIMD extensions
1The MM registers are aliased with the mantissa part of the FP registers
*

## Slide 243: a) AVX512 (2)
Extension of the available SIMD register space [155]
128
256
256
0

## Slide 244: a) AVX512 (3)
Evolution of the SP/FP and DP/FP performance in Intel's Core 2 lines [139]

## Slide 245: a) AVX512 (4)
Different versions of the AVX512 instruction set [155] Source: Intel SDE 8.40 (2017-06-01)
AVX-512-F: Foundation instructions
AVX-512-CD: Conflict Detect (loop vectorization with possible conflicts) AVX-512-BW: Support for 512-bit Word support AVX-512-DQ: More instructions for double/quad math operations
AVX-512-VL: Foundation plus <512-bit vector length support AVX-512-ER: Exponential and Reciprocal AVX-512-IFMA: Integer Fused Multiply Add with 52-bit precision AVX-512-PF: Prefetch Instructions AVX-512-VBMI: Vector Byte Manipulation Instructions AVX-512-4VNNIW: Vector Neural Network Instructions Word (variable precision) AVX-512-4FMAPS: Fused Multiply Accumulation Packed Single precision

## Slide 247: a) AVX512 (5)
Implementation of AVX512 in Skylake-SP [139]
*

## Slide 248: a) AVX512 (6)
Reduced turbo frequencies while running AVX code [139]
Note that turbo frequency limits are controlled on a per core basis.
*

## Slide 249: a) AVX512 (7)
Performance increase over SIMD generations [139]

## Slide 250
b) Re-architected L2/L3 cache hierarchy
Notes: 250

## Slide 251: b) Re-architected L2/L3 cache hierarchy (1)
b) Re-architected L2/L3 cache hierarchy [139]
*

## Slide 252: b) Re-architected L2/L3 cache hierarchy (2)
Cache inclusion policies between subsequent levels of a cache hierarchy
Inclusive cache levels
Non-inclusive cache levels
(Victim cache)
Exclusive cache-levels
Li
Li
Li+1
Li
If the cache levels are inclusive,
the higher cache level includes
the content of the underneath
cache level,
E.g. an inclusive L3 cache
contains the content of the
L2 cache
Li
Li+1
If the cache levels are exclusive,
a data item (in fact a cache line)
is contained either in the
higher or in the lower level
cache, but never in both.
Li
Li
Li+1
Li
In non-inclusive cache levels
the fact that a line is in level i
does not imply that it is also
in level i+1.
Changing the L3 cache inclusion policy from inclusive to non-inclusive -1
*

## Slide 253: b) Re-architected L2/L3 cache hierarchy (3)
Cache inclusion policies between subsequent levels of a cache hierarchy
Inclusive cache levels
Non-inclusive cache levels
(Victim cache)
Exclusive cache-levels
Inclusive cache levels reduce
the snoop traffic,
since in this case only the higher
cache level needs to be snooped.
Benefit of an exclusive cache
levels is the efficient use of the
cache space.
Their drawback is the not efficient
use of the cache space.
Examples
Intel's L3 caches in their
Haswell to Skylake lines
Intel's L2 caches in their
Pentium 4 and Core 2 based lines
Their drawback is that they
increase the snoop traffic
since in this case both
cache levels need to be
snooped.
Non-inclusive cache levels
seem to provide an efficient
cache use.
They need a more complex
cache coherency protocol.
AMD's L2 caches in their
Athlon (K6) and Opteron
based lines
Intel's L3 cache in their
Skylake-SP line
Assessing and use of cache inclusion policies
Benefit
Drawback
*

## Slide 254: b) Re-architected L2/L3 cache hierarchy (4)
 | L2 to L1 | L3 to L2 | L4 to L3
Core 2/ Penryn | Shared Non-inclusive |  | 
Nehalem/ Westmere | Private Non-inclusive | Shared Inclusive | 
Sandy Bridge/ Ivy Bridge | Private Non-inclusive | Shared Inclusive Sliced | 
Haswell Broadwell | Private Non-inclusive? | Shared Inclusive Sliced | Shared Non-inclusive
Skylake/ Kaby Lake | Private Non-inclusive? | Shared Inclusive Sliced | Shared Non-inclusive
Skylake-SP | Private Non-inclusive | Shared Non-inclusive Sliced | ??
All caches are write-back caches (WB) (except of the L1 Instruction cache).
L3 cache tags show which L1 and/or L2 caches hold the cache line
Inclusion policies of cache hierarchies in Intel's Core 2 lines [156]

## Slide 255: b) Re-architected L2/L3 cache hierarchy (5)
Changing the L3 cache inclusion policy from inclusive to non-inclusive -1
In the previous Skylake generation the inclusive L3 cache amounts to up to 2.5 MB/core
whereas the private L2 cache to 0.25 MB core and the L2 cache needs only about 10 %
of the L3 cache space.
By contrast, the Skylake-SP processor has an L3 cache of only 1.375 MB/core whereas
the private L2 caches amount to 1 MB/core.
Consequently, in the Skylake-SP processor the inclusive cache policy could not be used for
the L3 cache, it had to be modified to the non-inclusive policy since then the L2 cache
content is only partly included in the L3 cache.
*

## Slide 256: b) Re-architected L2/L3 cache hierarchy (6)
Non-inclusive vs. inclusive L3 [139]
Private
Shared
Shared
Private

## Slide 257: b) Re-architected L2/L3 cache hierarchy (7)
Cache misses in the Skylake-SP processor vs. the previous Broadwell-EP line -1 [139]
MPI: Misses Per Instruction

## Slide 258: b) Re-architected L2/L3 cache hierarchy (8)
Cache misses in the Skylake-SP processor vs. the previous Broadwell-EP line-2 [139]
MPI: Misses Per Instruction

## Slide 259: b) Re-architected L2/L3 cache hierarchy (9)
Skylake-SP's vs. Broadwell-EP cache latencies [139]

## Slide 260: b) Re-architected L2/L3 cache hierarchy (10)
Example cache parameters of Intel's Skylake microarchitecture [156]
1Software-visible latency will vary depending on access pattern and other factors

## Slide 261
c) 6 direct attached DDR4 memory channels
Notes: 261

## Slide 262: c) 6 direct attached DDR4 memory channels (1)
c) 6 direct attached DDR4 memory channels
Note that this kind of DRAM attachment is different from that implemented in the previous
Brickland 4S/8S platform.
*

## Slide 263: c) 6 direct attached DDR4 memory channels (2)
Attaching memory to Intel's servers (from Nehalem to Broadwell based servers) -2
Direct attaching memory to EN/EP servers
(EN: Entry level, EP: Efficient performance)
Attaching memory to Intel's servers
Indirect attaching memory to EX servers
(EX: Extendable (high-end))
Attaching up to 4 standard DDR memory channels
direct to to processor die
Attaching 8 standard DDR memory channels via
4 low line count serial or proprietary 64-bit parallel
channels (SMI) with memory buffers, while
two standard DDR memory channels
can be connected to each memory buffer (SMB)
C602J PCH
(Patsburg J)
QPI
1.1
QPI
1.1
QPI 1.1
QPI 1.1
DMI2
4xPCIe2
SMB
SMB
SMB
SMB
SMB
SMB
SMB
SMB
2x4 SMI2
channels
ME
Broadwell-EX
24C
Broadwell-EX
24C
PCIe 3.0
32
PCIe 3.0
32
Figure: Sandy Bridge-EP based server [142]
Figure: Part of a Broadwell-EX based server
*

## Slide 264: c) 6 direct attached DDR4 memory channels (3)
Line | Models | Core count | No. of memory channels | Kind of attachment | Socket | Intro
Nehalem-EP | E55xx | 2C-4C | 3xDDR3 | Direct attached standard DDR3 or DDR4 memory channels | LGA 1366 | 2009
Westmere-EP | E5600 | 2C-6C | 3xDDR3 |  | LGA 1366 | 2010
Sandy Bridge-EP | E5-26xx E5-46xx | 2C-8C 4C-8C | 4xDDR3 |  | LGA 2011 | 2012
Ivy Bridge-EP | E5-26xx v2 E5 46xx v2 | 4C-12C 4C-12C | 4xDDR3 |  | LGA 2011 | 2013 2014
Haswell-EP | E5-26xx v3 E5-46xx v3 | 4C-18C 6C-18C | 4xDDR4 |  | LGA 2011-3 | 2014 2015
Broadwell-EP | E5-26xx v4 E5-46xx v4 | 4C-22C 10C-22C | 4xDDR4 |  | LGA 2011-3 | 2016
Attaching memory to Intel's EP servers

## Slide 265: c) 6 direct attached DDR4 memory channels (4)
Line | Models | Core count up to | No. of mem. channels/ socket | Kind of attachment | Socket | Intro
Nehalem-EX | E6500 (2S) E75xx 4S/8S) | 8C | 8xDDR3 | 4 low line count serial channels (SMI) with mem. buffers, 2 DDR3 channels/ mem. buffer | LGA 1567 | 2010
Westmere-EX | E7-2800 E7-4800 E7-8800 | 10C | 8xDDR3 |  | LGA 1567 | 2011
Ivy Bridge-EX | E7-28xx v2 E7-48xx v2 E7-88xx v2 | 15C | 8xDDR3 | 4 low line count proprietary 64-bit parallel channels (SMI2) with memory buffers, 2 DDR3/4 channels/ mem. buffer | LGA 2011-1 | 2014
Haswell-EX | E7-48xx v3 E7-88xx v3 | 14C 18C | 8xDDR3/4 |  | LGA 2011-1 | 2015
Broadwell-EX | E7-48xx v4 E7-88xx v4 | 16C 22C | 8xDDR3/4 |  | LGA 2011-1 | 2016
Attaching memory to Intel's EX servers

## Slide 266: c) 6 direct attached DDR4 memory channels (5)
Attaching memory to Intel's servers (from Nehalem to Broadwell based servers) -1
Direct attaching memory
Attaching memory to Intel's servers
Indirect attaching memory to EX servers
Intel's Skylake-SP
(actually EX type) servers
Intel's EN/EP servers
Intel's EX servers
(No conversions needed)
*

## Slide 267: c) 6 direct attached DDR4 memory channels (6)
34x34 mm
45x42.5 mm
58.5x51.0 mm
76x56 mm
BGA 1226
LGA 1366
LGA 2011-3
LGA 3647
2xDDR2 standard
mem. channels
3xDDR3 standard
mem. channels
2x2 DDR4 standard
mem. channels
(2 on both side)
2x3 DDR4 standard
mem. channels
(3 on both side)
P965 GMCH
for Core 2
(2 cores)
Westmere-EP
(up to 6 cores)
Broadwell-EP
(up to 22 cores)
Skylake-SP
(up to 28 cores)
Sockets for direct attaching standard DDR memory channels to Intel's processors
Note that physical/electrical constraints limit the number of attachable memory channels
Source of the pictures [144]

## Slide 268: c) 6 direct attached DDR4 memory channels (7)
All these DIMMs
are 8-byte wide.
Pin counts of SDRAM to
DDR4 DIMMs
SDRAM
(SDR)
DDR
DDR2
DDR3
168-pin
184-pin
240- pin
240-pin
DDR4
284-pin
2.1 Overview of the Truland MP platform (1)
*
Notes: 268

## Slide 269: c) 6 direct attached DDR4 memory channels (8)
Implementation of the memory subsystem -1 [139]
2 memory controllers with 3 channels each resulting in 6 DDR channels.
Support of DDR4-2666, 2 DIMMs per channel
Figure: The memory subsystem [139]

## Slide 270: c) 6 direct attached DDR4 memory channels (9)
Implementation of the memory subsystem -2 [146]
Up to 1.5 TB memory capacity per socket, assuming 2 128 GB DIMMs.
> 60 % increase in memory bandwidth per socket compared to Xeon E5 v4 (Broadwell-EP)

## Slide 271
d) Mesh architecture
Notes: 271

## Slide 272: d) Mesh architecture (1)
d) Mesh architecture [143]
*

## Slide 273: d) Mesh architecture (2)
Broadwell-EX's ring architecture vs. Skylake-SP's mesh architecture [139]

## Slide 274: d) Mesh architecture (3)
Mesh architecture - more detailed [147]

## Slide 275: d) Mesh architecture (4)
Benefits of the mesh architecture
Higher performance
Lower latencies
Optimized for data sharing
*

## Slide 276
Interconnection style of Intel’s many core and multi-core processors
d) Mesh architecture (5)
Interconnection style of Intel’s many and multi-core processors
Ring architecture
Mesh (2D grid) architecture
Sony/Toshiba/IBM Cell (2006): 8 cores
Tile processor (2007): 80 cores
SCC (2010): 48 cores
Larrabee (2009). 24-32 cores (cancelled)
Xeon Phi
Knights Ferry (2010): 32 cores
Knights Corner (2012): 57-61 cores
Xeon Phi
Knights Landing (2016): up to 72 cores
Nehalem-EX (Beckton) (2010) up to 8 cores
All Sandy Bridge lines (2011) up to 8 cores
All Ivy Bridge lines (from 2012 on) up to 15 cores
to
All Broadwell lines (from 2014 on) up to 24 cores
Skylake (2015) up to 4 cores
Skylake-X (HED) (2017) up to 18 cores
Skylake-SP (2017) up to 28 cores

## Slide 277: d) Mesh architecture (6)
Note
While using a ring architecture in their 57 - 61 core Knights Corner processor presumably,
Intel experienced very long and very different latencies for data sharing, this could led the firm
to switch to a mesh architecture in their next Xeon Phi line.
Obviously, a mesh architecture has less and less different latencies for sharing data between
cores than a ring architecture (see below).
Figure: Contrasting ring and mesh architectures for data sharing between cores [143]
*

## Slide 278: d) Mesh architecture (7)
The layout of the ring interconnect on the Knights Corner die [157]

## Slide 279: d) Mesh architecture (8)
Intel's Xeon Skylake-SP vs. AMD's Naples - Intel's presentation [147]

## Slide 280
e) UPI (Ultra Path interconnect)
Notes: 280

## Slide 281: e) UPI (Ultra Path interconnect) (1)
e) UPI (Ultra Path interconnect) [139]
UPI replaces QPI.
It provides faster links and improved message efficiency for the data packets, as seen below.
Figure: Improved data rate of the UPI interconnect vs. QPI {}
*

## Slide 282
f) In-package integrated OmniPath host fabric interface
Notes: 282

## Slide 283: f) In-package integrated OmniPath host fabric interface (1)
f) In-package integrated OmniPath host fabric interface -1 [146]
Implemented in the F-series of the Skylake-SP line, called also as the Skylake-F series.
The F-series are Platinum and Gold level (processors of the Skylake-SP line, as seen below.
Figure: Skylake-SP models with integrated OmniPath host fabric interface [146]
*

## Slide 284: f) In-package integrated OmniPath host fabric interface (2)
In-package integrated OmniPath host fabric interface -2 [146]
It aims at simplifying the implementation of processor clusters.
*

## Slide 285: f) In-package integrated OmniPath host fabric interface (3)
Figure: Example of a processor cluster [158]
Storage system
Interconnect
fabric
(Switches)
Processor nodes
Basic components of a processor cluster [158]
Interconnect fabrics are used e.g. in processor clusters or supercomputers
They interconnect processor nodes and also processor nodes with the storage system.
*

## Slide 286
Possible layout of processor nodes [159]
f) In-package integrated OmniPath host fabric interface (4)
Interconnect fabric
CPU
CPU
CPU
CPU
CPU
CPU
Processor nodes
*

## Slide 287
Possible high speed interconnection technologies
Ethernet based
Fibre channels (FC) based
InfiniBand (FC) based
OmniPath based
f) In-package integrated OmniPath host fabric interface (5)

## Slide 288
Servers
Storage
s
s
Example: Processor cluster with InfiniBand based interconnect fabric and host and
target channel adapters, called also fabric interfaces [160]
Interconnect Fabric
f) In-package integrated OmniPath host fabric interface (6)

## Slide 289
Evolution of InfiniBand based high speed interconnect technologies to OmniScale
Infiniband (InfiniBand Trade Association. 1999)
TrueScale (Qlogic 2008)
(HPC Enhanced version of InfiniBand)
1/2012 Intel acquires QLogic’s TrueScale business
At the 2014 International Supercomputing Conference Intel announces both
Knights Landing and
the OmniScale interconnect fabric
11/2014 Intel renames OmniScale to OmniPath
f) In-package integrated OmniPath host fabric interface (7)
06/2016 Intel's Knights Landing line with in-package integrated OmniPath host channel adapter
07/2017 Intel's Xeon Skylake-SP line with in-package integrated OmniPath host channel adapter

## Slide 290: f) In-package integrated OmniPath host fabric interface (8)
Omni-Path Architecture Overview [167]
*

## Slide 291
Implementation alternatives of the Host Fabric Interfaces (HFI)
Implementation
on a separate card
In-package integration
(Implementation as a
Multi-Chip Package (MCM))
On-chip integration
1. Gen. Knights Landing
with OmniScale HCA
Skylake-F
2. Gen. Knights Landing
with OmniScale HCA
Previous systems
with TrueScale
Examples:
Evolution of the implementation of Host Channel Adapters called Fabric Controllers
in OmniScale
f) In-package integrated OmniPath host fabric interface (9)
*

## Slide 292: f) In-package integrated OmniPath host fabric interface (10)
System software needed for an interconnection fabric [161]

## Slide 293
g) New socket (LGA 3647)
Notes: 293

## Slide 294: g) New socket (LGA 3647) (1)
g) New socket (LGA 3647) [144]
58.5x51.0 mm
76x56 mm
LGA 2011
LGA 3647
2x2 DDR4 standard
mem. channels
(2 on both side)
2x3 DDR4 standard
mem. channels
(3 on both side)
Broadwell-EP
Broadwell-EX
Skylake-SP
Xeon Phy x200 (Knights Landing)
Broadwell-EP
Broadwell-EX
4 SMI2 serial
memory links
Skylake-SP

## Slide 295: g) New socket (LGA 3647) (2)
Skylake-SP socket with heatsink [144]

## Slide 296: g) New socket (LGA 3647) (3)
The Skylake-SP socket vs. the Broadwell-EP socket [144]

## Slide 297
5. References
Notes: 297

## Slide 298: 5. References (1)
[1]: Radhakrisnan S., Sundaram C. and Cheng K., „The Blackford Northbridge Chipset for the
Intel 5000”, IEEE Micro, March/April 2007, pp. 22-33
[2]: Next-Generation AMD Opteron Processor with Direct Connect Architecture – 4P Server
Comparison, http://www.amd.com/us-en/assets/content_type/DownloadableAssets/4P_
Server_Comparison_PID_41461.pdf
[3]: Intel® 5000P/5000V/5000Z Chipset Memory Controller Hub (MCH) – Datasheet,
Sept. 2006. http://www.intel.com/design/chipsets/datashts/313071.htm
[4]: Intel® E8501 Chipset North Bridge (NB) Datasheet, Mai 2006,
http://www.intel.com/design/chipsets/e8501/datashts/309620.htm
[5]: Conway P & Hughes B., „The AMD Opteron Northbridge Architecture”, IEEE
MICRO, March/April 2007, pp. 10-21
[6]: Intel® 7300 Chipset Memory Controller Hub (MCH) – Datasheet, Sept. 2007,
http://www.intel.com/design/chipsets/datashts/313082.htm
[7]: Supermicro Motherboards, http://www.supermicro.com/products/motherboard/
[8]: Sander B., „AMD Microprocessor Technologies,” 2006,
http://www.ewh.ieee.org/r4/chicago/foxvalley/IEEE_AMD_Meeting.ppt
[9]: AMD Quad FX Platform with Dual Socket Direct Connect (DSDC) Architecture,
http://www.asisupport.com/ts_amd_quad_fx.htm
[10]: Asustek motherboards - http://www.asus.com.tw/products.aspx?l1=9&l2=39
http://support.asus.com/download/model_list.aspx?product=5&SLanguage=en-us

## Slide 299: 5. References (2)
[11]: Kanter, D. „A Preview of Intel's Bensley Platform (Part I),” Real Word Technologies,
Aug. 2005, http://www.realworldtech.com/page.cfm?ArticleID=RWT110805135916&p=2
[12]: Kanter, D. „A Preview of Intel's Bensley Platform (Part II),” Real Word Technologies,
Nov. 2005, http://www.realworldtech.com/page.cfm?ArticleID=RWT112905011743&p=7
[13]: Quad-Core Intel® Xeon® Processor 7300 Series Product Brief, Intel, Nov. 2007
http://download.intel.com/products/processor/xeon/7300_prodbrief.pdf
[14]: „AMD Shows Off More Quad-Core Server Processors Benchmark” X-bit labs, Nov. 2007
http://www.xbitlabs.com/news/cpu/display/20070702235635.html
[15]: AMD, Nov. 2006 http://www.asisupport.com/ts_amd_quad_fx.htm
[16]: Rusu S., “A Dual-Core Multi-Threaded Xeon Processor with 16 MB L3 Cache,” Intel, 2006,
http://ewh.ieee.org/r5/denver/sscs/Presentations/2006_04_Rusu.pdf
[17]: Goto H., Intel Processors, PCWatch, March 04 2005,
http://pc.watch.impress.co.jp/docs/2005/0304/kaigai162.htm
[18]: Gilbert J. D., Hunt S., Gunadi D., Srinivas G., “The Tulsa Processor,” Hot Chips 18, 2006,
http://www.hotchips.org/archives/hc18/3_Tues/HC18.S9/HC18.S9T1.pdf
[19]: Goto H., IDF 2007 Spring, PC Watch, April 26 2007,
http://pc.watch.impress.co.jp/docs/2007/0426/hot481.htm

## Slide 300: 5. References (3)
[20]: Hruska J., “Details slip on upcoming Intel Dunnington six-core processor,” Ars technica,
February 26, 2008, http://arstechnica.com/news.ars/post/20080226-details-slip-on-
upcoming-intel-dunnington-six-core-processor.html
[21]: Goto H., 32 nm Westmere arrives in 2009-2010, PC Watch, March 26 2008,
http://pc.watch.impress.co.jp/docs/2008/0326/kaigai428.htm
[22]: Singhal R., “Next Generation Intel Microarchitecture (Nehalem) Family:
Architecture Insight and Power Management, IDF Taipeh, Oct. 2008,
http://intel.wingateweb.com/taiwan08/published/sessions/TPTS001/FA08%20IDF
-Taipei_TPTS001_100.pdf
[23]: Smith S. L., “45 nm Product Press Briefing,”, IDF Fall 2007,
ftp://download.intel.com/pressroom/kits/events/idffall_2007/BriefingSmith45nm.pdf
[24]: Bryant D., “Intel Hitting on All Cylinders,” UBS Conf., Nov. 2007,
http://files.shareholder.com/downloads/INTC/0x0x191011/e2b3bcc5-0a37-4d06-
aa5a-0c46e8a1a76d/UBSConfNov2007Bryant.pdf
[25]: Barcelona's Innovative Architecture Is Driven by a New Shared Cache,
http://developer.amd.com/documentation/articles/pages/8142007173.aspx
[26]: Larger L3 cache in Shanghai, Nov. 13 2008, AMD,
http://forums.amd.com/devblog/blogpost.cfm?threadid=103010&catid=271
[27]: Shimpi A. L., “Barcelona Architecture: AMD on the Counterattack,” March 1 2007,
Anandtech, http://www.anandtech.com/cpuchipsets/showdoc.aspx?i=2939&p=1

## Slide 301: 5. References (4)
[28]: Rivas M., “Roadmap update,”, 2007 Financial Analyst Day, Dec. 2007, AMD,
http://download.amd.com/Corporate/MarioRivasDec2007AMDAnalystDay.pdf
[29]: Scansen D., “Under the Hood: AMD’s Shanghai marks move to 45 nm node,”
EE Times, Nov. 11 2008,
http://www.eetimes.com/news/latest/showArticle.jhtml?articleID=212002243
[30]: 2-way Intel Dempsey/Woodcrest CPU Bensley Server Platform, Tyan,
http://www.tyan.com/tempest/training/s5370.pdf
[31]: Gelsinger P. P., “Intel Architecture Press Briefing,”, 17. March 2008,
http://download.intel.com/pressroom/archive/reference/Gelsinger_briefing_0308.pdf
[32]: Mueller S., Soper M. E., Sosinsky B., Server Chipsets, Jun 12, 2006,
http://www.informit.com/articles/article.aspx?p=481869
[33]: Goto H., IDF, Aug. 26 2005,
http://pc.watch.impress.co.jp/docs/2005/0826/kaigai207.htm
[34]: TechChannel, http://www.tecchannel.de/_misc/img/detail1000.cfm?pk=342850&
fk=432919&id=il-74145482909021379
[35]: Intel quadcore Xeon 5300 review, Nov. 13 2006, Hardware.Info,
http://www.hardware.info/en-US/articles/amdnY2ppZGWa/Intel_quadcore_Xeon_
5300_review
[36]: Wasson S., Intel's Woodcrest processor previewed, The Bensley server platform debuts,
Mai 23, 2006, The Tech Report, http://techreport.com/articles.x/10021/1

## Slide 302: 5. References (5)
[37]: Enderle R., AMD Shanghai “We are back! TGDaily, November 13, 2008,
http://www.tgdaily.com/content/view/40176/128/
[38]: Clark J. & Whitehead R., “AMD Shanghai Launch, Anandtech, Nov. 13 2008,
http://www.anandtech.com/showdoc.aspx?i=3456
[39]: Chiappetta M., AMD Barcelona Architecture Launch: Native Quad-Core, Hothardware,
Sept. 10, 2007,
http://hothardware.com/Articles/AMD_Barcelona_Architecture_Launch_Native_
QuadCore/
[40]: Hachman M., “AMD Phenom, Barcelona Chips Hit By Lock-up Bug,”, ExtremeTech,
Dec. 5 2007, http://www.extremetech.com/article2/0,2845,2228878,00.asp
[41]: AMD Opteron™ Processor for Servers and Workstations, http://amd.com.cn/CHCN/Processors/ProductInformation/0,,30_118_8826_8832,
00-1.html
[42]: AMD Opteron Processor with Direct Connect Architecture, 2P Server Power Savings
Comparison, AMD,
http://enterprise.amd.com/downloads/2P_Power_PID_41497.pdf
[43]: AMD Opteron Processor with Direct Connect Architecture, 4P Server Power Savings
Comparison, AMD,
http://enterprise.amd.com/downloads/4P_Power_PID_41498.pdf
[44]: AMD Opteron Product Data Sheet, AMD,
http://pdfs.icecat.biz/pdf/1868812-2278.pdf

## Slide 303: 5. References (6)
[45]: Images, Xtreview,
http://xtreview.com/images/K10%20processor%2045nm%20architec%203.jpg
[46]: Kanter D., “Inside Barcelona: AMD's Next Generation, Real World Tech., Mai 16 2007,
http://www.realworldtech.com/page.cfm?ArticleID=RWT051607033728
[47]: Kanter D,, “AMD's K8L and 4x4 Preview, Real World Tech. June 02 2006,
http://www.realworldtech.com/page.cfm?ArticleID=RWT060206035626&p=1
[48]: Kottapali S., Baxter J., “Nehalem-EX CPU Architecture”, Hot Chips 21, 2009,
http://www.hotchips.org/archives/hc21/2_mon/HC21.24.100.ServerSystemsI-Epub/
HC21.24.122-Kottapalli-Intel-NHM-EX.pdf
[49]: Kahn O., Piazza T., Valentine B., “Technology Insight: Intel next Generation
Microarchitecture Codename Sandy Bridge, IDF, San Francisco, Sept. 2010
[50]: Piazza T., Jiang H., “Intel Next Generation Microarchitecture Codename Sandy Bridge:
Processor Graphics, IDF, San Francisco, Sept. 2010
[51]: Braun-Protte T., “Intel die neuste Generation”, March 2010,
https://sp.ts.fujitsu.com/dmsp/docs/02_fujitsu_intel_server_cpu.pdf
[52]: De Gelas J., The Intel Xeon E7-8800 v3 Review: The POWER8 Killer?, AnandTech,
May 8 2015, http://www.anandtech.com/show/9193/the-xeon-e78800-v3-review
[53]: Tyan Confidential, Tempest i5000VF S5370, 2-way Intel Dempsey/Woodcrest CPU
Bensley Server Platform, http://www.tyan.com/tempest/training/s5370.pdf

## Slide 304: 5. References (7)
[55]: Neiger G., Santoni A., Leung F., Rodgers D., Uhlig R., Intel® Virtualization Technology:
Hardware support for efficient processor virtualization, Aug. 10 2006, Vol. 10, Issue 3,
http://www.intel.com/technology/itj/2006/v10i3/1-hardware/1-abstract.htm
[56]: Intel Software Networks: Forums,
http://software.intel.com/en-us/forums/showthread.php?t=56802
[57]: Wikipedia: x86 virtualization, 2011,
http://en.wikipedia.org/wiki/X86_virtualization#Intel_virtualization_.28VT-x.29
[54]: Intel 5520 Chipset and Intel 5500 Chipset, Datasheet, March 2009,
http://www.intel.com/content/www/us/en/chipsets/5520-5500-chipset-ioh-datasheet.html
[58]: Sharma D. D., Intel 5520 Chipset: An I/O Hub Chipset for Server, Workstation, and High
End Desktop, Hotchips 2009, http://www.hotchips.org/archives/hc21/2_mon/
HC21.24.200.I-O-Epub/HC21.24.230.DasSharma-Intel-5520-Chipset.pdf
[59]: Morgan T. P., Intel's future Sandy Bridge Xeons exposed, May 30 2011, The Register,
http://www.theregister.co.uk/2011/05/30/intel_sandy_bridge_xeon_platforms/page2.html
[60]: Gilbert J. D., Hunt S. H., Gunadi D., Srinivas G., The Tulsa Processor: A Dual Core Large
Shared-Cache Intel Xeon Processor 7000 Sequence for the MP Server Market Segment,
Aug 21 2006, http://www.hotchips.org/archives/hc18/3_Tues/HC18.S9/HC18.S9T1.pdf
[61]: Intel Server Board Set SE8500HW4, Technical Product Specification, Revision 1.0,
May 2005, ftp://download.intel.com/support/motherboards/server/sb/se8500hw4_board
_set_tpsr10.pdf

## Slide 305: 5. References (8)
[62]: Mitchell D., Intel Nehalem-EX review, PCPro,
http://www.pcpro.co.uk/reviews/processors/357709/intel-nehalem-ex
[64]: Intel Xeon Processor E7-8800/4800/2800 Product Families, Datasheet Vol. 1 of 2,
April 2011, http://www.intel.com/Assets/PDF/datasheet/325119.pdf
[63]: Nagaraj D., Kottapalli S.: Westmere-EX: A 20 thread server CPU, Hot Chips 2010
http://www.hotchips.org/uploads/archive22/HC22.24.610-Nagara-Intel-6-Westmere-EX.pdf
[65]: Supermicro P4QH6 / P4QH8 User’s Manual, 2002,
http://www.supermicro.com/manuals/motherboard/GC-HE/MNL-0665.pdf
[66]: Intel Xeon Processor 7500/6500 Series, Public Gold Presentation, March 30 2010,
http://cache-www.intel.com/cd/00/00/44/64/446456_446456.pdf
[67]: Supermicro X8QB6-F / X8QBE-F User’s Manual, 2010,
http://files.siliconmechanics.com/Documentation/Rackform/iServ/R413/Mainboard/MNL
-X8QB-E-6-F.pdf
[68]: Rusu & al.: A 45 nm 8-Core Enterprise Xeon Processor, IEEE journal of Solid State Circuits,
Vol. 45, No. 1, Jan. 2010, pp. 7-14
[69]: Jafarjead B., “Intel Core Duo Processor,” Intel, 2006,
http://masih0111.persiangig.com/document/peresentation/behrooz%20jafarnejad.ppt
[70]: Keutzer K., Malik S., Newton R., Rabaey J., Sangiovanni-Vincentelli A., System Level Design:
Orthogonalization of Concerns and Platform-Based Design, IEEE Transactions on
Computer-Aided Design of Circuits and Systems, Vol. 19, No. 12, Dec. 2000, pp.?????

## Slide 306: 5. References (9)
[71]: Perich D., Intel Volume platforms Technology Leadership, Presentation at HP World 2004,
http://98.190.245.141:8080/Proceed/HPW04CD/papers/4194.pdf
[72]: Krazit T., Intel Sheds Light on 2005 Desktop Strategy, IDG News Service, Dec. 07 2004,
http://pcworld.about.net/news/Dec072004id118866.htm
[73]: Molka D., Hackenberg D., Schöne R., Müller M. S., Memory Performance and Cache
Coherency Effects on an Intel Nehalem multiprocessor System, Proc. 18th Int. Conf.
on Parallel Architectures and Compilation, Techniques, PACT 2009,
http://doi.ieeecomputersociety.org/10.1109/PACT.2009.22
[74]: Radhakrishnan S., Chinthamani S., Cheng K., The Blackford Northbridge Chipset for
Intel 5000, IEEE MICRO, March-April 2007, pp. 22-33
[75]: Rolf T., Cache Organization and Memory Management of the Intel Nehalem Computer
Architecture, University of Utah, Dec. 2009, http://rolfed.com/nehalem/nehalemPaper.pdf
[76]: Levinthal D., Performance Analysis Guide for Intel Core i7 Processor and Intel Xeon 5500
processors, Version 1.0, 2008
http://software.intel.com/sites/products/collateral/hpc/vtune/performance_analysis_
guide.pdf
[79]: Gavrichenkov I., Workstation Processors Duel: AMD Opteron against Intel Xeon, Page 5
12/21/2005,
http://www.xbitlabs.com/articles/cpu/display/opteron-xeon-workstation_5.html
[78]: 3.6GHz 2MB 800MHz Intel Xeon Processor SL7ZC C8511, http://store.flagshiptech.com/
products/3.6GHz-2MB-800MHz-Intel-Xeon-Processor-SL7ZC-C8511.html
[77]: Ryszard Sommefeldt R., Intel Xeon 3.4GHz ['Nocona' core], 18th Aug, 2004, http://www.hexus.net/content/item.php?item=822&page=1&search=reas

## Slide 307: 5. References (10)
[80]: Glaskowsky P.: Investigating Intel's Lynnfield mysteries, cnet News, Sept. 21. 2009,
http://news.cnet.com/8301-13512_3-10357328-23.html
[81]: Kurd & al., Westmere: A Family of 32 nm IA Processors, Proc. ISSCC 2010, pp. 96-98
[82]: Miller M. J.,Intel Previews ISSCC: 6-Core Gulftown Processor, Feb 03, 2010, http://
forwardthinking.pcmag.com/chips/282694-intel-previews-isscc-6-core-gulftown-processor
[83]: Hill D., Chowdhury M., Westmere Xeon-56xx “Tick” CPU, Hot Chips 22, 2010,
http://www.hotchips.org/uploads/archive22/HC22.24.620-Hill-Intel-WSM-EP-print.pdf
[84]: Pawlowski S.: Intelligent and Expandable High- End Intel Server Platform, Codenamed
Nehalem-EX, IDF 2009
[85]: Intel Sandy Bridge Review, Bit-tech, Jan. 3 2011,
http://www.bit-tech.net/hardware/cpus/2011/01/03/intel-sandy-bridge-review/1
[86]: Kahn O., Piazza T., Valentine B.: Technology Insight: Intel Next Generation
Microarchitecture Codename Sandy Bridge, IDF 2010
extreme.pcgameshardware.de/.../281270d1288260884-bonusmaterial-pc- games-
ardware-12-2010-sf10_spcs001_100.pdf
[87]: Inkley B., Tetrick S., Intel Multi-core Architecture and Implementations, IDF, Session
MATS002, March 7 2006
[88]: Smith S. L., Intel Roadmap Overview, IDF Fall, Aug. 20 2008
http://download.intel.com/pressroom/kits/events/idffall_2008/SSmith_briefing_roadmap.pdf
[89]: Intel Public Roadmap; Business Platforms for Desktop, Mobile & Data Center, H1’ 2011
http://www.2ncinesil.com/download/Public%20Roadmap%201H%202011.pptx

## Slide 308: 5. References (11)
[90]: Rusu S., „Circuit Technologies for Multi-Core Processor Design,” April 2006,
http://www.ewh.ieee.org/r6/scv/ssc/April06.pdf
[91]: Goto H., IDF, Aug. 26 2005,
http://pc.watch.impress.co.jp/docs/2005/0826/kaigai207.htm
[92]: TechChannel, http://www.tecchannel.de/_misc/img/detail1000.cfm?pk=342850&
fk=432919&id=il-74145482909021379
[94]: Morgan T. P., Intel's future Sandy Bridge Xeons exposed, The Register, May 30. 2011,
http://www.theregister.co.uk/2011/05/30/intel_sandy_bridge_xeon_platforms
[95]: Gelsinger P., Keynote, IDF Spring 2005, March 2005,
http://www.intel.com/pressroom/kits/events/idfspr_2005/index.htm
[93]: Sandy Bridge, http://en.wikipedia.org/wiki/Sandy_Bridge
[96]: Kuppuswamy, R. C al., Over one million TPCC with a 45nm 6-core Xeon® CPU,
IEEE International Solid-State Circuits Conference - Digest of Technical Papers,
ISSCC 2009, Feb. 2009, pp. 70 - 71,71a
[97]: Perich D., Intel Volume Platforms Technology Leadership, Solutions and Technology
Conference, HP World 2004,
http://www.openmpe.com/cslproceed/HPW04CD/papers/4194.pdf
[98]: De Gelas J., Westmere-EX: Intel Improves their Xeon Flagship, AnandTech, April 6 2011,
http://www.anandtech.com/show/4259/westmereex-intels-flagship-improves
[99]: Starke W.J., POWER7: IBM’s Next Generation, Balanced POWER Server Chip, Hot Chips 21,
http://www.hotchips.org/wp-content/uploads/hc_archives/hc21/3_tues/HC21.25.800.
ServerSystemsII-Epub/HC21.25.835.Starke-IBM-POWER7SystemBalancev13_display.pdf

## Slide 309: 5. References (12)
[101]: Intel Server System SSH4 Board Set, Technical Product Specification, Oct. 2003,
http://download.intel.com/support/motherboards/server/ssh4/ssh4_tps.pdf
[102]: Haas J. & Vogt P., Fully buffered DIMM Technology Moves Enterprise Platforms to the
Next Level, Technology Intel Magazine, March 2005, pp. 1-7
[103]: Ganesh B., Jaleel A., Wang D., Jacob B., Fully-Buffered DIMM Memory Architectures:
Understanding Mechanisms, Overheads and Scaling, 2007,
https://ece.umd.edu/~blj/papers/hpca2007.pdf
[100]: Intel E8500 Chipset eXternal Memory Bridge (XMB), Datasheet, March 2005,
http://www.intel.co.id/content/dam/doc/datasheet/e8500-chipset-external-memory-
bridge-datasheet.pdf
[104]: Smith S. L., Quad-Core Press Briefing, IDF 2006,
http://www.intel.com/pressroom/kits/quadcore/qc_pressbriefing.pdf
[105]: Smith S.L., Intel Enterprise Roadmap, IDF 2010
[106]: Intel 7500 Chipset, Datasheet, March 2010,
http://www.intel.com/content/dam/doc/datasheet/7500-chipset-datasheet.pdf
[107]: 7500/7510/7512 Scalable Memory Buffer, Datasheet, April 2011,
http://www.intel.com/content/www/us/en/chipsets/7500-7510-7512-scalable-memory-
buffer-datasheet.html
[108]: X8QB6-LF User Manual, Supermicro

## Slide 310: 5. References (13)
[110]: Morgan T. P., Intel (finally) uncages Nehalem-EX beast, The Register, March 30 2010,
http://www.theregister.co.uk/2010/03/30/intel_nehalem_ex_launch/?page=2
[111]: Morgan T. P., Intel Puts More Compute Behind Xeon E7 Big Memory, The Platform,
May 5 2015, http://www.theplatform.net/2015/05/05/intel-puts-more-compute-behind-
xeon-e7-big-memory/
[112]: Niederste-Berg M., 28 core Skylake EP/EX plattform comes into view, Hardware LUXX,
26 May 2015, http://www.hardwareluxx.com/index.php/news/hardware/cpu/35474-
28-core-skylake-epex-plattform-comes-into-view.html
[109]: Baseboard management controller (BMC) definition, TechTarget, May 2007,
http://searchnetworking.techtarget.com/definition/baseboard-management-controller
[113]: Intel C102/C104 Scalable Memory Buffer, Datasheet, Febr. 2014,
http://www.intel.com/content/dam/www/public/us/en/documents/datasheets/c102-c104-
scalable-memory-buffer-datasheet.pdf
[114]: Intel Xeon Processor E7-8800/4800 V3 Product Family, Technical Overview, May 21 2015,
https://software.intel.com/en-us/articles/intel-xeon-processor-e7-88004800-v3-product-
family-technical-overview
[115]: X10QBi Platform with X10QBi Baseboard, User’s manual, Supermicro, 2014,
ftp://ftp.supermicro.com/CDR-X10-Q_1.00_for_Intel_X10_Q_platform/MANUALS/X10QBi.
pdf
[116]: Rusu S., Muljono H., Ayers D., Tam S., A 22nm 15-core enterprise Xeon processor family,
IEEE ISSC Journal, Vol. 50, Issue 1, Jan. 2015

## Slide 311: 5. References (14)
[118]: Chiappetta M., Intel Launches Xeon E7-8800 and E7-4800 v3 Processor Families,
Hot Hardware, May 5 2015,
http://hothardware.com/reviews/intel-launches-xeon-e7-v3-family-of-processors
[119]: Broadwell-EX/EP disappear from the latest Intel roadmap, AnandTech Forums,
http://forums.anandtech.com/showthread.php?t=2439161
[117]: Esmer I., Ivybridge Server Architecture: A Converged Server, Aug. 2014, Hot Chips 2014,
http://www.hotchips.org/wp-content/uploads/hc_archives/hc26/HC26-12-day2-epub/
HC26.12-8-Big-Iron-Servers-epub/HC26.13.832-IvyBridge-Esmer-Intel-IVB%20Server%
20Hotchips2014.pdf
[120]: Accelerate Big Data Insights with the Intel Xeon Processor E7-8800/4800 v3 Product
Families, Product Brief, 2015,
http://www.intel.com/newsroom/kits/xeon/e7v3/pdfs/Xeon_E7v3_ProductBrief.pdf
[121]: Accelerating Silicon Design with the Intel Xeon Processor E7-8800 v3 Product Family, 2015,
http://www.intel.com/content/dam/www/public/us/en/documents/product-briefs/xeon-
processor-e7-8800-v3-brief.pdf
[122]: Broadwell-EX/EP disappeared from Intel's enterprise roadmaps, Linus Tech Tips,
July 16 2015, http://linustechtips.com/main/topic/409185-broadwell-exep-disappeared-
from-intels-enterprise-roadmaps/
[123]: van Monsjou D., Massive Leak shows details on Skylake Xeon Chips, Overclock3D,
May 25 2015, http://www.overclock3d.net/articles/cpu_mainboard/massive_leak_shows_
details_on_skylake_xeon_chips/1

## Slide 312: 5. References (15)
[124]: Server duel: Xeon Woodcrest vs. Opteron Socket F, Tweakers, 7 September 2006,
http://tweakers.net/reviews/646/2/server-duel-xeon-woodcrest-vs-opteron-socket-f-
post-mortem-netburst.html
[125]: Papazian I. E. & al., Ivy Bridge Server: A Converged Design, IEEE MICRO, March-April
2015, pp. 16-25,
http://ieeexplore.ieee.org/xpl/articleDetails.jsp?reload=true&arnumber=7091791
[126]: Gao Y., HPC Workload Performance Tuning on POWER8 with IBM XL Compilers and Libraries,
SPXXL/Scicomp Summer Workshop 2014, http://spscicomp.org/wordpress/wp-content/
uploads/2014/05/gao-IBM-XL-compilers-for-POWER8-Scicomp-2014.pdf
[127]: New Xeon Processor Numbering, More Than Just a Number, Intel.com, April 5 2011,
https://communities.intel.com/community/itpeernetwork/datastack/blog/2011/04/05/
new-xeon-processor-numbering-more-than-just-a-number
[128]: Pirzada U., Intel Launches Its 14nm Broadwell-EX Platform,WCCF Tech, 07 June 2016,
http://wccftech.com/intel-broadwell-ex-xeon-e7-8890-24-cores/
[129]: Karedla, R., Intel Xeon E5-2600 v3 (Haswell) Architecture & Features, Intel, 2014,
http://repnop.org/pd/slides/PD_Haswell_Architecture.pdf
[130]: Syamalakumari S., Intel® Xeon® Processor E7-8800/4800 V3 Product Family Technical
Overview, Intel, May 21 2015,
https://software.intel.com/en-us/articles/intel-xeon-processor-e7-88004800-v3-product
-family-technical-overview
[131]: Rotem E. et al., Multiple Clock and Voltage Domains for Chip Multi Processors,
Proc. 42nd Annual IEEE/ACM International Symposium on Microarchitecture (MICRO)
December 12–16, 2009, New York, NY, USA.

## Slide 313: 5. References (16)
[132]: Gianos C., Intel Xeon Processor E5-2600 v3 Product Family Architectural Overview,
Intel, Nov. 16, 2014,
https://www.yumpu.com/en/document/view/34127638/intelr-xeonr-processor-
e5-2600-v3-overview-for-sc14
[133]: US 2014/0229750 A1 Patent application Method and apparatus for per core performance
states, Filed March 13 2012, Published Aug. 14 2014
[134]: Klemm M., Programming and Tuning for Intel® Xeon® Processors, Intel, 2015,
https://www.dkrz.de/Nutzerportal-en/doku/training/introduction-to-mistral-july-2014/
Programming_and_Tuning_for_Intel_Xeon_Processors_2015-07-01_M.Klemm.pdf?lang=en
[135]: https://en.wikipedia.org/wiki/RC_circuit
[136]: Samsung Memory DDR4 SDRAM, Broshure, Samsung, 2015,
http://www.samsung.com/semiconductor/global/file/insight/2015/11/DDR4_Brochure_
Nov-15-0.pdf
[137]: Hibben M., Will IBM Sell Its Mainframe Business? Seeking Alpha, Jul. 20, 2016
http://seekingalpha.com/article/3989959-will-ibm-sell-mainframe-business?auth_
param=djq9a:1bovpmu:2be6695ecca2e22ac60039ce2a123ea7
[138]: Intel QuickPath Interconnect Electrical Architecture Overview, Intel, 2010,
http://jamesstovalldesign.files.wordpress.com/2012/08/pages-from-intel_qpied_final_
03-18-10.pdf
[139]: Kumar A., Trivedi M., Intel Xeon Scalable Processor Architecture Deep Dive, June 12 2017,
https://www.primeline-solutions.de/files/intel-xeon-scalable-architecture-deep-dive_1.pdf

## Slide 314: 5. References (17)
[140]: De Gelas J., Cutress I., Sizing Up Servers: Intel's Skylake-SP Xeon versus AMD's EPYC
7000 - The Server CPU Battle of the Decade?, AnandTech, July 11 2017,
http://www.anandtech.com/show/11544/intel-skylake-ep-vs-amd-epyc-7000-cpu-battle-
of-the-decade/7
[141]: De Gelas J., The Intel Xeon E5 v4 Review: Testing Broadwell-EP With Demanding Server
Workloads, AnandTech, March 31 2016,
http://www.anandtech.com/print/10158/the-intel-xeon-e5-v4-review
[142]: Intel Xeon Processor E5-1600/E5-2600/E5-4600 Product Families, Datasheet, Vol. One,
May 2012, https://www.intel.com/content/dam/www/public/us/en/documents/datasheets/
xeon-e5-1600-2600-vol-1-datasheet.pdf
[143]: Intel Xeon Scalable Platform, Newsroom, 2017,
https://newsroom.intel.com/newsroom/wp-content/uploads/sites/11/2017/07/intel-xeon-
scalable-processors-overview.pdf
[144]: Kennedy P., Intel Xeon Scalable Processor Family Platform Level Overview, July 11 2017,
STH, https://www.servethehome.com/intel-xeon-scalable-processor-family-platform-
level-overview/
[145]: Shrater J., Intel's new innovation Engine Enables Differentiatied Firmware, Aug. 19 2015,
https://embedded.communities.intel.com/thread/12385
[146]: Shrout R., Intel Xeon Scalable Processor Launch - New Architecture, New Platform for
Data Center, PC Perspective, July 11 2017, https://www.pcper.com/reviews/Processors/
Intel-Xeon-Scalable-Processor-Launch-New-Architecture-New-Platform-Data-Center

## Slide 315: 5. References (18)
[147]: Chiappetta M., Intel Xeon Scalable Debuts: Dual Xeon Platinum 8176 With 112 Threads
Tested, Hot Hardware, July 11 2017,
https://hothardware.com/reviews/intel-xeon-scalable-processor-family-review
[148]: Hruska J., AMD Epyc Faces Off With Intel Skylake-SP Xeon in Massive Server Battle,
ExtremeTech, July 12 2017, https://www.extremetech.com/computing/252262-amd-
epyc-faces-off-intel-skylake-sp-xeon-massive-server-battle
[149]: Intel Xeon Scalable Platform, Product Brief, Intel, July 2017,
https://newsroom.intel.com/newsroom/wp-content/uploads/sites/11/2017/07/intel-
xeon-scalable-processors-product-brief.pdf
[150]: Safavi M., Thermal Design And NEBS Compliance, Electronics Cooling, Febr. 1 2006,
https://www.electronics-cooling.com/2006/02/thermal-design-and-nebs-compliance/
[151]: Morgan T. P., The X86 Battle Lines Drawn With Intel’s Skylake Launch, The Next Platform,
July 11 2017,
https://www.nextplatform.com/2017/07/11/x86-battle-lines-drawn-intels-skylake-launch/
[152]: Alcorn P., Intel Introduces New Mesh Architecture For Xeon And Skylake-X Processors,
Tom’s Hardware, June 15 2017, http://www.tomshardware.com/news/intel-mesh-
architecture-skylake-x-hedt,34806.html
[153]: Morgan T. P., Big Iron Xeons Get A Broadwell Compute And Memory Boost, The Next
Platform, June 6 2016, https://www.nextplatform.com/2016/06/06/big-iron-xeons-get-
broadwell-compute-memory-boost/

## Slide 316: 5. References (19)
[154]: Mulnix D., Intel Xeon Processor Scalable Family Technical Overview, June 22 2017,
https://software.intel.com/en-us/articles/intel-xeon-processor-scalable-family-technical-
overview
[155]: Cutress I., The Intel Skylake-X Review: Core i9 7900X, i7 7820X and i7 7800X Tested,
AnandTech, June 19 2017, http://www.anandtech.com/print/11550/the-intel-skylakex-
review-core-i9-7900x-i7-7820x-and-i7-7800x-tested
[156]: Intel 64 and IA-32 Architectures Optimization Reference Manual, June 2016,
https://www.intel.com/content/dam/www/public/us/en/documents/manuals/64-ia-32-
architectures-optimization-manual.pdf
[157]: Intel Xeon Phi Coprocessor Datasheet, Nov. 2012, http://www.intel.com/content/dam/
www/public/us/en/documents/product-briefs/xeon-phi-datasheet.pdf
[158]: Deploying HPC Cluster with Mellanox InfiniBand Interconnect Solutions, Reference Design,
June 2014, http://www.mellanox.com/related-docs/solutions/deploying-hpc-cluster-with-
mellanox-infiniband-interconnect-solutions.pdf
[159]: Wardrope I., High Performance Computing - Driving Innovation and Capability, 2013,
http://www2.epcc.ed.ac.uk/downloads/lectures/IanWardrope.pdf
[160]: QLogic TrueScale InfiniBand, the Real Value, Solutions for High Performance Computing,
Technology Brief, 2009,
http://www.transtec.de/fileadmin/Medien/pdf/HPC/qlogic/qlogic_techbrief_truescale.pdf
[161]: Intel Scalable System Framework Intel HPC Developer Conference, Nov. 12-13 2016,
http://itoc.sjtu.edu.cn/wp-content/uploads/2016/05/Intel-Omni-Path-in-HPC.pdf

## Slide 317: 5. References (20)
[162]: Ng P. K., High-End Desktop Platform Design Overview for the Next Generation Intel
Microarchitecture (Nehalem) Processor, IDF Taipei, 2008, TDPS001, Intel,
http://intel.wingateweb.com/taiwan08/published/sessions/TDPS001/FA08%20IDF-
Taipei_TDPS001_100.pdf
[163]: [63]: Nagaraj D., Kottapalli S.: Westmere-EX: A 20 thread server CPU, Hot Chips 2010
http://www.hotchips.org/uploads/archive22/HC22.24.610-Nagara-Intel-6-Westmere-EX
.pdf
[164]: Next-Generation AMD Opteron Processor with Direct Connect Architecture – 4P Server
Comparison, http://www.amd.com/us-en/assets/content_type/DownloadableAssets/4P_
Server_Comparison_PID_41461.pdf
[166]: Haas J. & Vogt P., Fully buffered DIMM Technology Moves Enterprise Platforms to the
Next Level, Technology Intel Magazine, March 2005, pp. 1-7
[165]: Supermicro Motherboards, X6QT8, User Manual,
https://www.supermicro.com/products/motherboard/Xeon7000/E8501/X6QT8.cfm
[167] Supermicro Motherboards, MNL-1594X6QT8, User Manual,
https://www.supermicro.com/manuals/motherboard/C606_602/MNL-1594.pdf
[167]: Birrittella M. S., Intel Omni-Path Architecture Technology Overview, August 2015,
http://www.hoti.org/hoti23/slides/rimmer.pdf
[168] Danowitz A. & al. CPU DB: Recording Microprocessor History, Communications of the
ACM, Vol. 55 No. 4, Pages 55-63
[169]: Haas, J. & Vogt P., Fully buffered DIMM Technology Moves Enterprise Platforms to the
Next Level,” Technology Intel Magazine, March 2005, pp. 1-7

## Slide 318: 5. References (21)
[170]: A New Day for the Datacenter, Presentation at AMD Financial Analyst Day, May 16 2017,
http://ir.amd.com/phoenix.zhtml?c=74093&p=irol-analystday

## Slide 319
2x/6 y
3x/4 y

## Slide 320
ARM
(MCs are linked via the
CCN-5xx interconects
to the platform
2012-2014)
16C/32C/48C