## Slide 1
Sima Dezső
Nov. 2017
(Ver. 2.3)
 Sima Dezső, 2017
The mobile boom

## Slide 2
1. Emergence and spread of smartphones
Contents
3. Key requirements of mobile devices
5. Conclusions
6. References
2. Emergence and spread of tablets
4. How leading IT vendors addressed the mobile boom?

## Slide 3
1. Emergence and spread of smartphones
Notes: 3

## Slide 4: 1. Emergence and spread of smartphones ()
1. Emergence and spread of smartphones
The traditional computer market around 1995
Desktops
Embedded
computer devices
Main computer market segments around 1995
Intel’s Pentium 4 lines
AMD’s Athlon lines
ARM’s lines
Servers
Intel’s Xeon lines
AMD’s Opteron lines
E.g.
From about 1995: spreading of laptops (aka notebooks) (portable computers)
*

## Slide 5: 1. Emergence and spread of smartphones (1)
Emergence of mobile devices from about 2005 [2]
The mobile boom
Netbooks: Small size laptops (e.g. with a display size of 10" or smaller.)

## Slide 6: 1. Emergence and spread of smartphones (2)
Emergence of smartphones-1
Forerunners of smartphones emerged already
at the beginning of the 2000’s, like Nokia’s 7650
(shipped in 2002).
Figure: Nokia’s 7650 [39]
The 7650 became the first widely available phone
with camera and color screen but supported
no video.
It was the first Nokia phone running under
the Symbian OS.

## Slide 7: 1. Emergence and spread of smartphones (3)
The emergence of smartphones is often
contributed to the BlackBerry Pearl 8100
line of the Canadian firm RIM
(Research in Motion)[5].
This phone – shipped in 2006 - supported
beyond a camera also video and became
very popular in the US.
It was run under the BlackBerry OS.
Emergence of smartphones-2
Figure: RIM’s BlackBarry Perl 8100
(2006) [38]
*

## Slide 8: 1. Emergence and spread of smartphones (4)
Early spread of smartphones-1
In 2007 Apple’s iPhone gave a strong momentum for rapid spreading of
smartphones.
It run under the iPhone OS (renamed later to iOS in 2010).
Figure: Steve Jobs introducing the iPhone at MacWorld Expo in 1/2007 [47]
*

## Slide 9: 1. Emergence and spread of smartphones (5)
Remark
After the introduction of iPhone (2007) Steve Ballmer (CEO of Microsoft) said in an
interview [20]:
“There's no chance that the iPhone is going to get any significant market share.
No chance…
But if you actually take a look at the 1.3 billion phones that get sold, I'd prefer
to have our software (Windows Phone) in 60% or 70% or 80% of them, than
I would to have 2% or 3%, which is what Apple might get”.

## Slide 10: 1. Emergence and spread of smartphones (6)
Early spread of smartphones-2
Google’s Android was unveiled also in 2007 with first Android-powered phones
sold in 10/2008 [6].
*

## Slide 11: 1. Emergence and spread of smartphones (7)
Emergence and rapid increase of smartphone sales 2005-2011 [4]
A: Actual values
E: Estimated
PC sales: Desktop + Notebook sales

## Slide 12: 1. Emergence and spread of smartphones (8)
Worldwide unit shipments of smartphones 2007-2016 [28]

## Slide 13: 1. Emergence and spread of smartphones (10)
Huawei: Chinese Oppo: Chinese Vivo: Chinese
Worldwide smartphone market share in 2014-2017 (in unit shipments) [69]

## Slide 14: 1. Emergence and spread of smartphones (11)
Worldwide market share of smartphone OSs in 2009-2015 [42]
*

## Slide 15: 1. Emergence and spread of smartphones (12)
Remember
After the introduction of iPhone (2007) Steve Ballmer (CEO of Microsoft) said in an
interview [20]:
“There's no chance that the iPhone is going to get any significant market share.
No chance…
But if you actually take a look at the 1.3 billion phones that get sold, I'd prefer
to have our software in 60% or 70% or 80% of them, than I would to have 2%
or 3%, which is what Apple might get”.

## Slide 16: 1. Emergence and spread of smartphones (13)
Worldwide smartphone OS market share in 2014-2017 (unit shipments) [70]

## Slide 17: 1. Emergence and spread of smartphones (14)
Worldwide market share of application processors in 1H 2017 used in
smartphones (based on revenue) [71]
Vendor | Market share | Processor lines (examples) | ISA
Qualcomm (USA) | 42 % | Snapdragon line 200-805 Snapdragoon 808-845 | ARMv7 ARMv8
Apple (USA) | 18 % | Apple A4-A6X Apple A7-A11 | ARMv7 ARMv8
MediaTek (Taiwan) | 18 % | Helio x10 Helio X20 | ARMv7 ARMv8
Samsung (S. Korea) |  | Exynos 5 line Exynos 7/8/9 | ARMv7 ARMv8
[Source: Strategy Analytics]
*
ARMv7: 32-bit
ARMv8: 64-bit

## Slide 18: 2. Emergence and spread of smartphones (15)
Model | Released | Technology | CPU | Word length bit | Clock rate (up to) | Connectivity
835 | Q2/2017 | 10 nm | 4+4 Kryo 280 | 64 | 2.45 GHz | integrated LTE + RF
821 | Q3/2016 | 14 nm | 2+2 Kryo | 64 | 1.4 GHz | integrated LTE + RF
820 | Q4/2015 | 14 nm | 2+2 Kryo | 64 | 2.2 GHz | integrated LTE + RF
810 | H2/2014 | 20 nm | 4x ARM Cortex A57 + 4x ARM Cortex A53 | 64 | 2.0 GHz | integrated LTE + RF
808 | H1/2015 | 20 nm | 2x ARM Cortex A57 + 4x ARM Cortex A53 | 64 | 2.0 GHz | integrated LTE + RF
805 | Q1/2014 | 28 nm | 4x Krait 450 | 32 | 2.7 GHz | integrated LTE + RF
801 | Q4/2013 | 28 nm | 4x Krait 400 | 32 | 2.5 GHz | integrated LTE + RF
800 | Q2/2013 | 28 nm | 4x Krait 400 | 32 | 2.3 GHz | integrated LTE + RF
600 | Q1/2013 | 28 nm | 4x Krait 300 | 32 | 1.9 GHz | integrated WiFi
410 | 1H/2014 | 28 nm | 4x ARM Cortex A53 | 64 | 1.4 GHz | integrated LTE + RF
400 | Q4/2013 | 28 nm | 4x Krait 300 or 4x ARM Cortex A7 | 32 | 1.7 GHz 1.4 GHz | integrated LTE + RF
200 | 2013 | 28 nm | 4x ARM Cortex A5 or 4x ARM Cortex A7 | 32 | 1.4 GHz 1.2 GHz | integrated 3G + RF
Main features of the Qualcomm Snapdragoon lines
RF: Radio Frequency Front End implemented as a separate chip

## Slide 19: 1. Emergence and spread of smartphones (16)
Intel's efforts to enter the mobile market [Based on 2]
2008
2-wide
in-order
4-wide
out-of-order
2-wide
in order
2-wide
out-of-order
2-wide
out-of-order
Introduction of the Atom line targeting the mobile market

## Slide 20: 1. Emergence and spread of smartphones (17)
Intel’s Atom platforms targeting smartphones (based on [33])
Clover Trail+
(2013)
Medfield
(2012)
Merrifield
(2014)
Moorefield
(2014)
Morganfield
(2016)
Lexington
(2013)
Slayton
(2014)
Riverton
(2015)
Binghampton
(2016)
Z2580-2520
2xSaltwell
32 nm
+XMM 6268/6360/7160
Z2420
1xSaltwell
32 nm
+XMM 6265
Z2480/2460
1xSaltwell
32 nm
+XMM 6260
Z34x0
2xSilvermont
22 nm
+XMM 7160/7260
Z3xxx
2xSilvermont
22 nm
+A-GOLD 620
Zxxxx
2xAirmont
14 nm
+?
Zxxx
2xAirmont
14 nm
+?
Z35xx
4xSilvermont
22 nm
+XMM 7260/2/35
Z5xxx
4xGoldmont
14 nm
+XMM 7360
Performance (not to scale)
Morestown
(2010)
Z6xx
1xBonnell
45 nm
+Wireless
module
Cancelled
in 04/2016

## Slide 21: 1. Emergence and spread of smartphones (18)
Intel’s XMM line including a 3G/4G modem an a transceiver (on two chips)
3G/4G modem
RF Transceiver
Figure: Implementation
example of the
XMM7160 [46]

## Slide 22: 1. Emergence and spread of smartphones (19)
Intel’s effort to optimize their devices from the software point of view
In their 2012 Investor meeting (5/2012) Intel revealed that more than 3000
engineers are working on OS support, among them about 1200 engineers
are dedicated to Android, as indicated below [11].

## Slide 23: 1. Emergence and spread of smartphones (20)
Despite great efforts Intel could not become one of the 5 largest suppliers
of smartphone application processors.
According to industry sources in 2014 Intel achieved less than 1 % share in revenue
in smartphone application processors.
Intel’s share in smartphone application processors in 2014 [54]
*

## Slide 24: 1. Emergence and spread of smartphones (21)
Intel's withdrawal from the mobile market
In 4/2016 Intel announced their withdrawal from the mobile market.
*

## Slide 25
2. Emergence and spread of tablets
Notes: 25

## Slide 26: 2. Emergence and spread of tablets (1)
Picture of a DynaBook
Picture of two kids sitting in the grass with Dynabooks
2. Emergence and spread of tablets
An early vision of tablets targeting children - the Dynabook []
In 1972 at the ACM National Conference Alan Kay from the Xerox Palo Alto Research
Center (PARC) introduced a Personal Computer for Children, called the Dynabook.
“This note speculates about the emergence of personal, portable information manipulators and their effects when used by both children and adults. Although it should be read as science fiction, current trends in miniaturization and price reduction almost guarantee that many of the notions discussed will actually happen in the near future."
*

## Slide 27: 2. Emergence and spread of tablets (2)
In a talk given at the Center for Design Innovation Steve Jobs envisioned tablets
already in 1983 saying
”Apple’s strategy is really simple. What we want to do is we want to put an
incredibly great computer in a book that you can carry around with you and learn
how to use in 20 minutes.
... And we really want to do it with a radio link in it so you don’t have to hook up
to anything and you’re in communication with all of these larger databases and
other computers” [19].
Steve Jobs vision of tablets
*

## Slide 28: 2. Emergence and spread of tablets (3)
In an interview in 2010 Kay said that "Jobs has known about the
Dynabook idea and the interim-Dynabook (called the PARC Alto)
for several decades".
Here we note that Steve Jobs and Apple engineers visited PARC in 1979.
While asking in the cited interview "whether he felt that Jobs
had stolen the idea for the iPad" Kay denied such a thought.
In fact, there is a difference in the usage models of Dynabook and IPad.
Dynabook represented an idea of active computing e.g. with children
programming it by means of its keyboard in Smalltalk.
By contrast, iPad is built for passive computing while using applications
downloaded e.g. from the App Store.
The relation of the Dynabook and iPad [73]

## Slide 29: 2. Emergence and spread of tablets (4)
In 2010 Apple’s iPad was introduced with 9.7 “ screen, touch screen and Wi-Fi or
additionally wireless 3G broadband internet connection (mobile internet connection),
operating under iOS [12].
Designs leading to the rapid spreading of tablets around 2010
From 2009 on Android-based tablets arrived the market from many vendors.
Figure: Steve Jobs introducing the iPad in 2010 [12]
*

## Slide 30: 2. Emergence and spread of tablets (5)
Implementation alternatives of tablets -1 [8]

## Slide 31: 2. Emergence and spread of tablets (6)
Intel’s Surface Pro 3
used as a laptop [22]
Intel’s Surface Pro 3
used as a tablet [23]
Implementation alternatives of tablets -2 [8]
2 in 1 tablets (≈ attachable keyboard + touchscreen)
Example: Windows Surface Pro 3 (8/2014)
Aim: Replacing laptops

## Slide 32: 2. Emergence and spread of tablets (7)
Besides smartphones, tablets and all their alternative designs (that provide also keyboard/mouse input, such as convertibles or 2 in 1 designs) have recently the highest growth potential, as indicated in the Figure below (12/1012) [3].
Desktops
Notebooks
Tablets
Figure: Yearly worldwide sales figures of desktops, notebooks and tablets [3]
Rapid increase of tablet sales in the first half of the 2010’s

## Slide 33: 2. Emergence and spread of tablets (8)
Worldwide shipment of laptops, desktop PCs and tablets from 2010 to 2016
as well as sale forecasts until 2021 (in million units) [35]
Source: Gartner

## Slide 34: 2. Emergence and spread of tablets (9)
Vendor | 2Q16 Unit Shipments | 2Q16 Market Share | 2Q15 Unit Shipments | 2Q15 Market Share | Year-Over-Year Growth
1. Apple | 10.0 | 25.8% | 11.0 | 24.9% | -9.2%
2. Samsung | 6.0 | 15.6% | 8.0 | 18.2% | -24.5%
3. Lenovo | 2.5 | 6.6% | 2.5 | 5.6% | 3.1%
4. Huawei | 2.2 | 5.6% | 1.3 | 2.9% | 71.0%
5. Amazon | 1.6 | 4.0% | 0.1 | 0.3% | 1208.9%
Others | 16.4 | 42.4% | 21.3 | 48.2% | -22.9%
Total | 38.7 | 100.0% | 44.1 | 100.0% | -12.3%
2016 worldwide tablet shipments (in million units) and market shares
by vendors [76]

## Slide 35: 2. Emergence and spread of tablets (10)
Global market share of tablet OS shipments 2010 - 2014 by quarter [25]
*

## Slide 36: 2. Emergence and spread of tablets (11)
Global market share of tablet OSs 2013-2017 and forecast until 2020 [88]

## Slide 37: 2. Emergence and spread of tablets (12)
Intel's platforms targeting tablets (based on [11])
Clover Trail
(2012)
Oak Trail
(2011)
Bay Trail
(2013)
Cherry Trail
(2015)
Willow Trail
(2016)
Atom X3
(Sophia 3G)
(2015)
Atom X3
(Sophia LTE)
(2015)
Z2760
2xSaltwell
32 nm
+XMM 6260
W
Z670/650
1xBonnell
45 nm
+ no XMM
W/MeeGo/A
Z37x0
4xSilvermont
22 nm
+XMM 6260/7160
W/A
C3000
2xSilvermont
28 nm
integrated 3G
modem
C3400
4xAirmont
28 nm
integrated LTE
modem
Z4xxx
4xAirmont
14 nm
+XMM 7160/7260
W/A
Z5xxx
4xGoldmont
14 nm
+XMM 7360
W/A
Performance (not to scale)
Menlow
(2008)
Z5xx
1xBonnell
45 nm
+ no XMM
W/Moblin
Cancelled
in 04/2016
W: Windows
A: Android

## Slide 38: 2. Emergence and spread of tablets (13)
Intel’s share in tablet application processors [35], [36], [56]
Intel ’s subsidies paid for OEMs
In the first years of 2010 Intel paid significant subsidies (~ 50 $/tablet) to
netbook and tablet manufacturers to achieve their switch from ARM based
processors to x86 Atom processors.
In 2015 Intel achieved the 3. place in the worldwide market share in
tablet application processor revenue, as the Table below shows.
Achieved market share in 2015 due to paying subsidies
Tablet application processors worldwide market share 2015 (revenue) [57] | 
Apple (USA) | 31 %
Qualcomm (USA) | 16 %
Intel (USA) | 14 %
MediaTek (Taiwan) | 
Samsung (S. Korea) | 
Table: Worldwide market share of application processors used in tablets in 2015
(based on revenue)
Subsidy: szubvenció
*

## Slide 39: 2. Emergence and spread of tablets (14)
Intel's losses on the mobile development in 2013 - 2014 [74]
Nevertheless, owing to subsidies Intel's mobile and communication division has lost
7 billion $ in the years 2013-2014 , as indicated in the next Figure [83].
Figure: Revenues/operating income of Intel's Mobile and Communications segment [83]

## Slide 40: 2. Emergence and spread of tablets (15)
Intel's withdrawal from the mobile market
Due to their high losses Intel first stopped paying subsidies and then in 4/2016
announced their withdrawal from the mobile market.
*

## Slide 41
3. Key requirements of mobile devices (tablets, smartphones)
Notes: 41

## Slide 42: 3. Key requirement of mobile devices (tablets, smartphones)
Key requirements of mobile devices (tablets, smartphones)
Connectivity
(3G/4G/Wi-Fi)
Low power operation
3. Key requirements of mobile devices (tablets, smartphones)
(Section 3.1)
(Section 3.2)
*

## Slide 43
3.1 Low power operation
Notes: 43

## Slide 44: 3.1 Low power operation (1)
3.1 Low power operation
It will be expressed
either by specifying the power consumption, e.g. the TDP value of
the processor in Watt,
or in in length of the operating hours of the device under given conditions.
Power consumption = Active power (Cdyn∗VCC2 ∗ fc) + Leakage power (VCC ∗ Ileak)
*

## Slide 45: 3.1 Low power operation (1b)
Contrasting the design paradigms of traditional and mobile processors
High performance/power
(Power efficiency)
(e.g. GFLOPS/Watt)
Traditional processors
Tablets and smartphones
Low power consumption
(Watt)
(Number of operating hours)
*

## Slide 46: 3.1 Low power operation (2)
Sustainable power for fanless tablets [78]
*

## Slide 47: 3.1 Low power operation (3)
Total platform power consumption
It results from the power consumption of the SOC, display, memory, network etc.
i.e. from any circuit that is mounted on the motherboard.

## Slide 48: 3.1 Low power operation (4)
Total power consumption of a tablet: Example one side of the iPad Air 2
motherboard [79]

## Slide 49: 3.1 Low power operation (5)
Example: Total power consumption of tablets
while running the (SunSpider 0.9.1 benchmark) [80]
NVidia T30
4+1x Cortex A9, 1.3 GHz)
Intel Atom Z2760
(2C, 1.8 GHz)
Qualcomm S4 (APQ8060A)
(2C 1.5 GHz)
SunSpider, is a mid-length JavaScript benchmark.

## Slide 50: 3.1 Low power operation (6)
Basic LC filter modified with an inline resistor
e.g. 20 mΩ
Measuring the power consumption of a CPU [80]

## Slide 51: 3.1 Low power operation (7)
SunSpider, is a mid-length JavaScript benchmark.
In the power consumption of Qualcomm's S4
the L2 cache is not taken into account.
NVidia T30
4+1x Cortex A9, 1.3 GHz)
Intel Atom Z2760
(2C, 1.8 GHz)
Qualcomm S4 (APQ8060A)
(2C 1.5 GHz)
Example: Power consumption of CPUs while running the (SunSpider 0.9.1
benchmark) [80]
*

## Slide 52: 3.1 Low power operation (7b)
Remark to the power management of the referenced processors [80]
The cores in both the dual core Atom and 4+1 core NVIDIA's Tegra 3 share the
sare voltage and frequency during power management.
Figure: Power consumption of the S4 while running the Sunspider 0.9.1 benchmark [80]
By contrast, the dual core Qualcomm's S4 make use of per core voltage and
frequency scaling, as indicated below.
In addition L2 has a separate voltage rail and can be power managed separately.

## Slide 53: 3.1 Low power operation (8)
Example: Total idle power consumption of tablets [80]
NVidia T30
4+1x Cortex A9, 1.3 GHz)
Intel Atom Z2760
(2C, 1.8 GHz)
Qualcomm S4 (APQ8060A)
(2C 1.5 GHz)

## Slide 54: 3.1 Low power operation (9)
Apple iPad: 32.4 Wh
Apple iPad Air: 32.4 Wh
Microsoft Surface RT: 31.5 Wh
Acer Iconia W510: 3.54 Ah (4.7 V)
Dell XPS 10: 28 Wh
Battery sizes of tablets - examples

## Slide 55: 3.1 Low power operation (10)
1.3 GHz 2C A6 (Swift, ARMv7)
1.5 GHz 2C MSM8960 (Krait 200, ARMv7)
1.6 GHz Atom Z2460 (x86-32)
Example: Power consumption of smartphones while running the (Kraken
Benchmark 2 [80]
*

## Slide 56: 3.1 Low power operation (11)
Example: AMD’s technologies to reduce power consumption (2008-2014) [27]

## Slide 57: 3.1 Low power operation (12)
Achieving low power consumption
In this point let’s focus on the microarchitecture of CPUs (processor cores).
*

## Slide 58: 3.1 Low power operation (13)
Key enablers of low power microarchitectures
Low clock frequency
Narrow microarchitecture
Key enablers of low power microarchitectures
(Section 3.1.2)
(Section 3.1.3)
*

## Slide 59: 3.1 Low power operation (14)
3.1.2 “Narrow” microarchitectures -1
Obviously, a narrow microarchitecture consumes less power than a wider one.
What does a narrow microarchitecture mean?
*

## Slide 60: 3.1 Low power operation (14b)
Microarchitecture of the cores of Sandy Bridge [90]
Example for the "width of a microarchitecture"
In-order
Front end
Out-of-order
parallel
Back end

## Slide 61: 3.1 Low power operation (14c)
3.1.2 “Narrow” microarchitectures -2
A suitable characteristics of the width of a microarchitecture is the width of its
front end, that can be characterized by the decode width.
We note that in a well designed microarchitecture all subsystems, like fetching,
decoding, renaming dispatching or issuing instructions are appropriately
fitted to each other.
To achieve low power consumption first application processors used in tablets
and smartphones were "thin" designs with a typical decode width of 2,
as shown in the next Figure.
*

## Slide 62: 3.1 Low power operation (15)
High performance
Mainstream
Low power
Key features of ARMv7 ISA based early microarchitectures (based on [14])

## Slide 63: 3.1 Low power operation (16)
We note that at the same time Intel's mainline processors had a 4-wide
microarchitecture, as indicated below, to provide high performance/power
(in terms of GFLOPS/Watt).
Figure: Width of Intel’s Core 2 (2006) to Broadwell (2014) microarchitetures
underlying servers to laptops [10]
64-bit
Intel
Core 2
to
Broadwell
“Narrow” microarchitectures -3

## Slide 64: 3.1 Low power operation (17)
Remarks
Evolution of the decode width in Intel's mainstream microarchitectures
up to the Pentium 4 (2000): 3-wide
beginning with the Core 2 (2006): 4-wide
beginning with the Skylake (2015): 5-wide
By contrast AMD's microarchitectures remained 3-wide until the K15 Bulldozer line
(2011).
This fact was a significant contributor to Intel's performance superiority.
*

## Slide 65: 3.1 Low power operation (18)
Evolution of the width of mobile microarchitectures -1
a) When ARM introduced the ARMv8-based (64-bit) processor line they increased
the microarchitecture width of their high-performance Cortex-A57 and the A72
processors from 2 to 3, to boost performance, as seen in the next Figure.
Advancements in IC technology and power management allowed to widen the
microarchitecture of mobiles without noticeable raising their power consumption,
as follows.
*

## Slide 66: 3.1 Low power operation (19)
High performance
Low power
Key features of ARMv8.0 ISA based microarchitectures (based on [14])

## Slide 67: 3.1 Low power operation (20)
ARM's also implemented their ARMv8.2-based high performance A75 processor
with a 3-wide microarchitecture.
Evolution of the width of mobile microarchitectures -2

## Slide 68: 3.1 Low power operation (21)
b) In 2014 a few papers (e.g. [48]) revealed that Apple's A6 (2013) has an
astonishingly wide (6-wide) dual-core microarchitecture (called Cyclon),
used in the iPad Air (see the next Figure).
Evolution of the width of mobile microarchitectures -3
*

## Slide 69: 3.1 Low power operation (22)
Apple’s Cyclone core, introduced in the A7 SOC (2013) [48]

## Slide 70: 3.1 Low power operation (23)
Name | Techn. | Cores | Launched | fc | Decode rate | Used in
A5X | 45 nm | 2x Cortex-A9 | 3/2011 | 1.0 GHz | 2 | iPad (3. gen.)
A6 | 32 nm | 2x Swift | 9/2012 | 1.3 GHz | 3 | iPhone 5/5C
A6X | 32 nm | 2x Swift | 10/2012 | 1.4 GHz | 3 | iPad (4th gen.)
A7 | 28 nm | 2x Cyclon | 09/2013 | 1.3 GHz | 6 | iPhone 5S iPad Mini 2/3
A7 | 28 nm | 2x Cyclon | 10/2013 | 1.4 GHz | 6 | iPad Air
A8 | 20 nm | 2x Typhoon | 09/2014 | 1.1 - 1.5 GHz | 6 | iPhone 6/6 Plus iPad Mini 4
A8X | 20 nm | 3x Typhoon | 10/2014 | 1.5 GHz | 6 | iPad Air 2
A9 | 14 nm | 2x Twister (Samsung) | 09/2015 | 1.85 GHz | 6 | iPhone 6S/6S Plus iPhone SE iPad (2017)
A9 | 16 nm | 2x Twister (TSMC) | 09/2015 | 1.85 GHz | 6 | 
A9X | 16 nm | 2x Twister | 11/2015 | 2.16 - 2.26 GHz | 6 | iPad Pro 12.9" iPad Pro 9.7"
A10 | 16 nm | 2x Hurricane (HP) 2x Zephyr (EE) | 09/2016 | 2.34 GHz | n.a. | iPhone 7/7 Plus iMac Pro (2017)
A10X | 10 nm | 3x Hurricane (HP) 3x Zephyr (EE) | 06/2017 | 2.36 GHz | n.a. | iPad Pro 10.5" iPad Pro 12.9"
A11 | 10 nm | 2x Monsoon (HP) 4x Mistral (EE) | 09/2017 | 2.40 GHz | n.a. | iPhone 8/8 Plus iPhone X
Main features of Apple's A5X to A11 processors
HP: High Performance core
EE: Energy Efficient core

## Slide 71: 3.1 Low power operation (24)
The performance of Apple's Cyclone based tablets while running the
Geekbench 3.2 benchmark [49]
3 Typhoon
cores
2014
2013
2 Cyclone
cores
K1
A8X

## Slide 72: 3.1 Low power operation (25)
c) In 2016 Samsung introduced their Galaxy S7 tablet and Galaxy Note 7
smartphone that were based (partly) on the Exynos 8890 that included
four Exynos M1 (Mongoose) cores with a 4-wide microarchitecture
as well as four Cortex-A15 cores.
Evolution of the width of mobile microarchitectures -4

## Slide 73: 3.1 Low power operation (26)
Intel lost Apple as a perspective buyer of their chips for the iPad line,
and the iPad Air 2 also severely hit the perspective of their not so successful
Atom line.
NVIDIA’s Tegra 4 chips were not successful, so the firm announced in 05/2014
that they will abandon the phone market.
Apple’s iPad Air 2 with its A8X processor and its GPU with 256 EUs became a very
powerful rival to NVIDIA's subsequent 64-bit K1 chip including a GPU with
192 EUs.
As a consequence, NVIDIA also gave up their tablet interests.
Implications of the extremely high performance of Apple’s A8X-based
iPad Air 2 (including 3 Typhoon cores) [50]
*

## Slide 74: 3.1 Low power operation (27)
NVidia's leaving the smartphone and tablet market in June 2016 [81]
In 6/2016 (at Computex) NVIDIA's CEO declared the firm's leaving the smartphone
and tablet market by saying:
: “We are no longer interested in that market”. He adds, “Anybody can build
smartphones, and we’re happy to enjoy these devices, but we’ll let someone else
build them”.
Instead NVIDIA became interested in designing in-car computers and car
infotainment systems.
*

## Slide 75: 3.1 Low power operation (28)
3.1.3 Low clock frequency-1
In addition: higher fc requires higher VCC (VCC ≈ const x fC).
Basics
Figure: Core voltage (VCC) vs. clock frequency (fC) for Intel’s Westmere processors [26]
Active power consumption = Cdyn∗VCC2 ∗ fc

## Slide 76: 3.1 Low power operation (29)
Relative high base clock frequency
(typically 2-4 GHz)
Traditional CPUs
Mobile CPUs
Relative low base clock frequency
(typically 1-2 GHz)
Low clock frequency-2
Higher fC
higher VCC
higher D
It follows
D ≈ fC3
*
Low power consumption
Higher allowed power budget

## Slide 77: 3.1 Low power operation (30)
TDP (W) | No. of cores | Graphics | No. of graphics EUs | eDRAM | Base frequency up to (GHz)
4.5 | 2 | HD 515 | 18 | -- | 1.2
15 | 2 | HD 540 | 48 | 64 MB | 2.2
15 | 2 | HD 520 | 24 | -- | 2.6
28 | 2 | HD 550 | 48 | 64 MB | 3.3
35 | 4 | HD 530 | 24 | -- | 2.8
45 | 4 | HD 530 | 24 | -- | 2.9
65 | 4 | HD 530 | 24 | -- | 3.4
91 | 4 | -- | -- | -- | 4.2
Example: Base frequency of Skylake models with different TDPs and
configurations (Based on data from [58])
Note that low TDP can be achieved first of all by reducing the core frequency and
limiting the computer resources (cores, GPU EUs) provided.
*

## Slide 78: 3.1 Low power operation (31)
Name | Techn. | Cores | Launched | fc | Decode rate | Used in
A5X | 45 nm | 2x Cortex-A9 | 3/2011 | 1.0 GHz | 2 | iPad (3. gen.)
A6 | 32 nm | 2x Swift | 9/2012 | 1.3 GHz | 3 | iPhone 5/5C
A6X | 32 nm | 2x Swift | 10/2012 | 1.4 GHz | 3 | iPad (4th gen.)
A7 | 28 nm | 2x Cyclon | 09/2013 | 1.3 GHz | 6 | iPhone 5S iPad Mini 2/3
A7 | 28 nm | 2x Cyclon | 10/2013 | 1.4 GHz | 6 | iPad Air
A8 | 20 nm | 2x Typhoon | 09/2014 | 1.1 - 1.5 GHz | 6 | iPhone 6/6 Plus iPad Mini 4
A8X | 20 nm | 3x Typhoon | 10/2014 | 1.5 GHz | 6 | iPad Air 2
A9 | 14 nm | 2x Twister (Samsung) | 09/2015 | 1.85 GHz | 6 | iPhone 6S/6S Plus iPhone SE iPad (2017)
A9 | 16 nm | 2x Twister (TSMC) | 09/2015 | 1.85 GHz | 6 | 
A9X | 16 nm | 2x Twister | 11/2015 | 2.16 - 2.26 GHz | 6 | iPad Pro 12.9" iPad Pro 9.7"
A10 | 16 nm | 2x Hurricane (HP) 2x Zephyr (EE) | 09/2016 | 2.34 GHz | n.a. | iPhone 7/7 Plus iMac Pro (2017)
A10X | 10 nm | 3x Hurricane (HP) 3x Zephyr (EE) | 06/2017 | 2.36 GHz | n.a. | iPad Pro 10.5" iPad Pro 12.9"
A11 | 10 nm | 2x Monsoon (HP) 4x Mistral (EE) | 09/2017 | 2.40 GHz | n.a. | iPhone 8/8 Plus iPhone X
Main features of Apple's A5X to A11 processors
HP: High Performance
EE: Energy Efficient

## Slide 79
3.2 Connectivity
Notes: 79

## Slide 80: 3.2 Connectivity (1)
3.2 Connectivity
Connectivity may include (depending on the device type)
LAN connectivity
Wi-Fi connectivity (coined after Hi-Fi)
mobile broadband connectivity (recently 3G/4G).
Subsequently, we will focus only on the mobile broadband connectivity.

## Slide 81: 3.2 Connectivity (2)
Simplified view of a platform providing mobile broadband connectivity [59]
PA: Power Amplifier LNA: Low Noise Amplifier Transceiver: Transmitter/Receiver
(DSP)
Modem + Application Processor
(if integrated implementation)
RF
LNA
Mixers
Modem: Actually a baseband
processor that runs under a
proprietary real-time OS).
It has two functions:
to performe modulation/
demodulation and
to manage the
communication
according to a protocol
Multiband: multiple frequency bands, e.g. 900/1800 MHz
Multimode: 3G/ 4G (LTE)
*

## Slide 82: 3.2 Connectivity (3)
Use of integrated
application processor and modem
Integration of the application processor and the modem
Qualcomm’s MSM product offerings
since ~ 1996
including their Snapdragon families
Use of discrete
application processor and modem
NVIDIA’s Tegra 2-4, K1 (since 2011)
NVIDIA’s Tegra 4i (2014)
MediaTek’s 6xxx/8xxx families (since ~ 2009)
except the 81xx line
MediaTek’s 81xx line (2013)
Integration of the application processor and the modem
Samsung’s Exynos 3/4/5/7 families
(since ~ 2010)
Integrating the modem onto the application processor die results in less costs and
shorter time to market.
Qualcomm pioneered this move designing integrated parts already about 1996.
Samsung’s Exynos 8 Octa 8890
(2015)
Apple’s own processor designs
(Swift (2012), Cyclone (2013)
Intel’s Atom line (2008)
except recent Atom X3 (Sophia (2015)
E.g.
Intel’s Atom X3 (Sophia) (2015)
*

## Slide 83: 3.2 Connectivity (4)
Example of using discrete application processor and modem: The iPhone 6+
PAD: Integrated Power Amplifier-Duplexer
The front side of the
logic board [60]

## Slide 84: 3.2 Connectivity (5)
Example of using an integrated application processor and a modem
(Qualcomm’s Snapdragon 820) [61]

## Slide 85: 3.2 Connectivity (6)
Worldwide market share of smartphone and tablet application processors
in 2015 (based on revenue) [34]
Smartphone application processors worldwide market share 2015 (revenue) | 
Qualcomm (USA) | 42 %
Apple (USA) | 21 %
MediaTek (Taiwan) | 19 %
Samsung (S. Korea) | 
Spreadtrum (China) | 
Tablet application processors worldwide market share 2015 (revenue) | 
Apple (USA) | 31 %
Qualcomm (USA) | 16 %
Intel (USA) | 14 %
MediaTek (Taiwan) | 
Samsung (S. Korea) | 
[Source: Related press releases of Strategy Analytics]
*

## Slide 86: 3.2 Connectivity (7)
Qualcomm provides single chip solutions
for feature phones, termed as
QSCs (Qualcomm Single Chips).
QSCs integrate the functions of
MSMs
RF Transmitters (RF Tx)
RF Receivers (RF Rx) and
Power manager ICs (PM)
as illustrated on the Figure left [62].
Integrating the application processor, the modem, RF transmitter,
RF receiver and power manager IC onto a single chip
It became also feasible for less demanding applications, e.g. for feature phones.
Example: Qualcomm’s QSCs (Qualcomm Single Chips)
Figure: Qualcomm’s integrated QSC [62]

## Slide 87: 3.2 Connectivity (8)
1GB LPDDR3-1600 SDRAM
Figure: Apple’s A7 PoP [63]
Remark on using PoP (Package on Package) memories
In Apple's processors the processor die and the memory die or dies are mounted
in the same package already since the Apple A4 (2007).
E.g. In Apple’s A7 Package-on-Package processor, as used in the iPhone 5s.
*

## Slide 88
4. How leading IT vendors addressed the mobile boom?
4.2 Microsoft’s response to the mobile boom
4.1 Intel’s and AMD’s response to the mobile boom
Notes: 88

## Slide 89
4.1 Intel’s and AMD’s response to the mobile boom
Notes: 89

## Slide 90: 4.1 Intel’s and AMD’s response to the mobile boom (1)
Intel’s and AMD’s traditional CPUs are designed for high performance/power,
consequently they are wide and power hungry,
but mobile devices require low power consumption, so
Intel’s and AMD’s traditional microarchitectures are not suited for mobile devices.
4.1 Intel’s and AMD’s response to the mobile boom-1
*

## Slide 91: 4.1 Intel’s and AMD’s response to the mobile boom (2) (1)
Total shipments of smartphones vs. PCs and tablets 2011-2017 [28]
Source: Gartner (2013)
Smartphone and tablet shipments
will vastly exceed PC shipments
(desktops and notebooks)
in a few years

## Slide 92: 4.1 Intel’s and AMD’s response to the mobile boom (3)
Intel and AMD were forced
to introduce novel narrow (i.e. 2-wide), low-power microarchitectures
for their CPUs and
clock them at a relative low rate.
To avoid shrinking market shares on the global processor market
and benefit from the rapidly increasing mobile market
Intel and AMD need processors that are competitive with ARM based designs.
Intel’s and AMD’s response to the mobile boom-2
*

## Slide 93: 4.1 Intel’s and AMD’s response to the mobile boom (4)
Evolution of Intel’s basic architectures [Based on 2]
2008
2-wide
in-order
4-wide
out-of-order
2-wide
in order
2-wide
out-of-order
2-wide
out-of-order

## Slide 94: 4.1 Intel’s and AMD’s response to the mobile boom (4)
Intel's market share achieved on the mobile market
In 2014 Intel achieved only less than 1 % share in revenue in smartphone
application processors [54].
By contrast, on the worldwide tablet market Intel achieved about 14 % market
share, albeit only due to paying subsidies for OEMs.
Nevertheless, owing to paying subsidies and due to low sales figures with mobile
products Intel lost about 7 billion $ in the years 2013-2014 [83] that lead to
Intel's withdrawal from the mobile market.
*

## Slide 95: 4.1 Intel’s and AMD’s response to the mobile boom (5)
Intel's withdrawal from the smartphone and mobil market
As Intel failed to gain traction in the mobile sector, in 4/2016 Intel announced
their withdrawal from the mobil market.
Intel's statement says [82]:
"I can confirm that the changes included canceling the Broxton platform as
well as SoFIA 3GX, SoFIA LTE and SoFIA LTE2 commercial platforms
to enable us to move resources to products that deliver higher returns and
advance our strategy.
These changes are effective immediately."
At the same time Intel laid off about 12000 employees (~ 11 % of their
workforce).
*

## Slide 96: 4.1 Intel’s and AMD’s response to the mobile boom (6)
Evolution of AMD’s basic architectures
2014
4/2014
2-wide
out-of-order
2-wide
out-of-order
2-wide
out-of-order
4-wide
out-of-order

## Slide 97: 4.1 Intel’s and AMD’s response to the mobile boom (7)
Cancellation of AMD's Cat line in 2015
Neither Intel nor AMD became successful on the mobile market, so beyond
Intel also AMD stopped their activities on this market.
The last core of AMD's Cat line was the Puma+ core (launched in 6/2015 in the
Carrizo-L APU).
In AMD's 2016 Mobility roadmap there is no sign of an APU powered by the
Puma+ core or a derivative of a core belonging to the Cat line, as seen in the
next Figure.
Instead AMD placed emphasis on Zen core based products.
*

## Slide 98: 4.1 Intel’s and AMD’s response to the mobile boom (8)
AMD's leaked mobility roadmap for 2015-2016 without indicating the
Puma core for 2016 [87]

## Slide 99: 4.1 Intel’s and AMD’s response to the mobile boom (9)
Nintendo Wii U (2012)
Sony Playstation 4 (2013)
Microsoft Xbox One (2013)
Microsoft Xbox one S (2016)
Microsoft Xbox One X (2017)
Ataribox (2017).
Use of AMD’s low power Jaguar and Puma architectures in game consoles
Most recent game consoles are based on AMD’s low power Jaguar architecture,
including
These consoles have a noticeable global market share, as indicated in the next
Figure.
*

## Slide 100: 4.1 Intel’s and AMD’s response to the mobile boom (10)
Global unit sales of current generation video game consoles 2008-2014 [64]
(in million units)

## Slide 101
4.2 Microsoft’s response to address the mobile boom
Notes: 101

## Slide 102: 4.2 Microsoft’s response to the mobile boom (1)
4.2 Microsoft’s response to address the mobile boom -1
Worldwide software revenues in 2013 [25]

## Slide 103: 4.2 Microsoft’s response to the mobile boom (2)
Microsoft's response to address the mobile boom
Introduction of
Windows based OSs
for smartphones
Vision to become
a devices and services
company
Microsoft's response to address the mobile boom -2
Widening the scope
of Windows to cover also touchscreen tablets
*

## Slide 104: 4.2 Microsoft’s response to the mobile boom (3)
a) Widening the scope of Windows to cover also touchscreen tablets -1
2012 Windows 8 it aims to cover PCs, notebooks and also tablets
2013 Windows 8.1
2014 Windows 8.1 with Bing for low cost devices
2014 Windows 9 skipped
2014 Windows 10 Technical Preview
2015 Windows 10 general availability
Market reflections: Windows 8 earned moderate success, Android and iOS
dominated further on the market for smartphones and tablets.
Windows 8 was Microsoft’s first try to cover the whole spectrum of computers from
servers through desktops and notebooks till touchscreen tablets by a single OS.
In 5/2014 Microsoft announced Windows 8.1 with the search engine Bing.
It will be delivered for hardware manufacturers for free.
Windows 8.1 is an upgrade for Windows 8.
OS releases covering touch screen devices as well:

## Slide 105: 4.2 Microsoft’s response to the mobile boom (3b)
Windows 10 is released in 07/2015, it provides an updated Start menu.
To encourage its adoption Microsoft made it available free of charge during its
first year of availability to users with genuine copies of Windows 7/Windows 8.1.
a) Widening the scope of Windows to cover also touchscreen tablets -2

## Slide 106: 4.2 Microsoft’s response to the mobile boom (3c)
Desktop Windows version market share worldwide [91]

## Slide 107: 4.2 Microsoft’s response to the mobile boom (3d)
Microsoft's and Qualcomm's cooperation resulting in the capability of the
Snapdragoon 835 to run under Windows 10
Benefit for Qualcomm
Possible use of the Snapdragoon 835 also in laptops allowing extended battery life,
fan-less designs and lighter devices vs. x86 systems.
Benefit for Microsoft
Gaining higher market share in laptop OSs
In 5/2017 major OEMs (including ASUS, HP and Lenovo) announced to develop
Snapdragoon 835 based laptops running under Windows 10 and including the
x16 LTE modem providing 1 Gbit download rate and all-day battery life [92].
Announced in 8/2016

## Slide 108: 4.2 Microsoft’s response to the mobile boom (3e)
Microsoft enhanced Windows 10 to emulate traditional x86 Windows32
applications.
Thus devices will be able to run x86 Windows 32 applications, like Chrome or
Photoshop or a large number of other applications.
Nevertheless, x86 Windows64 applications are not supported.
This is not a huge problem since not many applications have been compiled to
64-bit, and most that were also have a 32-bit version.
Microsoft emulates the CPU instruction set, but memory, storage or graphics
handling won't be emulated and handled natively by the OS.
Accordingly, CPU heavy applications will run slower than on x86-based machines.
At the moment there is no experience how far emulation will slow down running
x86 Windows32 applications.
Emulation of x86 Windows32 applications [93]

## Slide 109: 4.2 Microsoft’s response to the mobile boom (4)
b) Introduction of Windows based OSs for smartphones
2003 Windows Mobile 2003
It was based on the kernel of Microsoft's Windows CE.
Windows CE was an OS for embedded devices, optimized for minimal
memory).
Windows Phone 7
Despite Microsoft's efforts, Windows based phone OSs could not
achieve notable market share, as indicated in the next Figure.
Finally, in 10/2017 Intel cancelled Windows 10 Mobile.
Nokia's Lumia series of smartphones starting with the Lumia 800 (2011)
were based on Qualcomm's processors but run under the
Windows Phone (later the Windows 10 Mobile) OSs.
The Windows Phone 7 earned moderate success.
Windows Phone 8
Windows Phone 8.1
Windows 10 Mobile
Subsequent versions:

## Slide 110: 4.2 Microsoft’s response to the mobile boom (5)
Global market share of leading smartphone OSs in terms of sales figures
to end users from Q1 2009 to Q3 2015 [42]

## Slide 111: 4.2 Microsoft’s response to the mobile boom (6)
Microsoft's activities to become a devices and services company
Taking part in
the game console market
Introduction of the
Surface line of tablets
Entering the
phone business
c) Microsoft's vision to become a devices and services company
“I think that in a back-looking view, people would say we were a software company.
That's kind of how we were born.
I think when you look forward, our core capability will be software, (but)
you'll probably think of us more as a devices-and-services company.” [22]
Microsoft's vision to become a devices-and-services company
Ballmer (CEO of Microsoft in 9/2012):
*

## Slide 112: 4.2 Microsoft’s response to the mobile boom (7)
ca) Microsoft's participation in the game console market
Picture: The original Xbox console with the Controller
Source of the picture: https://en.wikipedia.org/wiki/Xbox
Microsoft created a family of video game consoles, dubbed as Xbox.
Main models of the Xbox family
2001: The original Xbox
2005: Xbox 360
2013: Xbox One
2016: Xbox One S
2017:Xbox One X
*

## Slide 113: 4.2 Microsoft’s response to the mobile boom (8)
Surface Pro lines
Microsoft’s Surface family of tablets
Surface lines
First Surface tablets are NVIDIA’s Tegra based
and run under Windows RT.
Recent Surface tablets are Intel’s Atom based
and are running under Windows 8.1
Surface Pro tablets are Core 2 based
and run under Windows 8
or subsequent Windows versions
High end models
Less expensive models
cb) Introduction of the Surface family of tablets
*
Since 2012
Since 2013

## Slide 114: 4.2 Microsoft’s response to the mobile boom (9)
Model | Intro | Processor | Word length | Core nr. | OS
Surface | 10/2012 | Tegra 3 | 32-bit | 4 | Windows RT
Surface 2 | 10/2013 | Tegra 4 | 32-bit | 5 | Windows RT
Surface 3 | 05/2015 | Atom X7-Z8700 Airmont core | 64-bit | 4 | Windows 8.1
Table: Microsoft’s ARM/Intel Atom-based Surface RT /Surface 2 tablets
Overview of Microsoft’s Surface tablets -1
Main features of Microsoft’s Surface tablet line
The exclusivity of Windows RT drastically limits app availability, and is one of the main reasons why sales of Surface tablets remained lower than expected [21].
Note that NVidia's Tegra processors are 32-bit ARMv7-A based.
In 2015 Microsoft dropped production of devices based on Windows RT.
Windows RT was a modified version of Windows 8 that targeted the ARMv7-A ISA.

## Slide 115: 4.2 Microsoft’s response to the mobile boom (10)
Model | Intro | Processor | Word length | Core nr. | OS
Surface Pro | 02/2013 | Ivy Bridge i5 | 64-bit | 2 | Windows 8 Pro
Surface Pro 2 | 10/2013 | Haswell i5 | 64-bit | 2 | Windows 8.1 Pro
Surface Pro 3 | 06/2014 | Haswell i3/i5/i7 | 64-bit | 2 | Windows 8.1 Pro
Surface Pro 4 | 10/2015 | Skylake-U i5 | 64-bit | 2 | Windows 10 Pro
Surface Pro 2017 | 06/2017 | Kaby Lake m3 | 64-bit | 2 | Windows 10 Pro
Table: Microsoft’s Intel Core 2-based Surface Pro tablets
Overview of Microsoft’s Surface tablets -2
Main features of Microsoft’s Surface Pro tablet line

## Slide 116: 4.2 Microsoft’s response to the mobile boom (11)
Example: Windows Surface Pro 3 (8/2014)
2 in 1 tablet 12”
Aim: Replacing laptops
Intel’s Surface Pro 3
used as a laptop [22]
Intel’s Surface Pro 3
used as a tablet [23]

## Slide 117: 4.2 Microsoft’s response to the mobile boom (12)
Further Surface products [84]

## Slide 118: 4.2 Microsoft’s response to the mobile boom (13)
Early financial performance of Microsoft’s Surface business [24]

## Slide 119: 4.2 Microsoft’s response to the mobile boom (14)
9/2013: Microsoft announces their plan to acquire the phone business of Nokia,
including the Lumia brand.
4/2014: Microsoft finalyses the acqisition by paying about 7 billion USD to Nokia,
and taking over about 25000 Nokia employees.
11/2014: Microsoft rebranded the Nokia Lumia line to Microsoft Lumia line.
cc) Microsoft's move to enter the phone business
*
About the same time when the sales figures of Google's Android surpassed those
of Nokia's that run the Symbian mobile OS, in 2/2011 Nokia set up a business
partnership with Microsoft and adopted Windows Phone as its primary platform
for their future smartphones, called Lumia.

## Slide 120: 4.2 Microsoft’s response to the mobile boom (15)
The first Microsoft branded Lumia phone (the Lumia 535 from 11/2014) [85]

## Slide 121: 4.2 Microsoft’s response to the mobile boom (16)
Microsoft's acquisition of Nokia's phone business did not seriously boost the sale
figures of Windows phone based Lumia devices, as indicated in the Figure below.
Figure: Quarterly sale figures of Lumia devices (million units) [85]
(Nokia introduced the Lumia brand for a series of smartphones running Windows phone)
Microsoft ackquires
Nokia's phone buiness
On the contrary, in about two years sale figures desreased below 1 % of the total
world sales of smartphones, as indicated in the Figure.
1 % of worldwide
smartphone sales
The outcome of Microsoft's Nokia deal -1
Rebranding the Nokia Lumia line
to Microsoft Lumia line

## Slide 122: 4.2 Microsoft’s response to the mobile boom (17)
In 7/2015 Microsoft restructured Microsoft Mobile and laid off 7200 employees.
In 5/2016 Microsoft made the decision to sell their feature phone business
to Foxconn (Taiwan), for 350 million USD.
As a consequence, 4500 Microsoft employes were moved to Foxconn.
At the same time Microsoft confirmed that it will continue to develop
Windows 10 Mobile, and support existing Lumia phones and ones built
by third-party phone makers [86].
In 10/2017 Intel cancelled Windows 10 Mobile.
The outcome of Microsoft's Nokia deal -2
Consequences of deminishing sales figures of Windows based Lumia phones
*

## Slide 123
5. Conclusions
Notes: 123

## Slide 124: 5. Conclusions (1)
5. Conclusions -1
new paradigms
new devices
new players
Informatics came into a transitional phase
*

## Slide 125: 5. Conclusions (2)
Established companies have to respond early, quick and in an appropriate way
to the new challenges, else…
8/2010 Intel acquires Infineon’s (former Siemens) Wireless Solutions business
8/2011 Google acquires Motorola Mobility
9/2013 Microsoft decides to purchase Nokia’s phone business
9/2013 BlackBerry lays off 4500 employees (~ 40% of their workforce)
6/2014 Broadcom decides to exit the baseband business
~ 2015 AMD leaves the mobile market
4/2016 Intel leaves the mobile market
5/2016 NVIDIA declares that they will moving out from the smartphone market
Conclusions- 2

## Slide 126: 5. Conclusions (3)
1/2011 AMD: Dirk Meyer
11/2012 Intel: Paul Otellini
8/2013 Microsoft: Steve Ballmer
Even the largest IT firms have a hard time to cope with as indicated by
resignation of AMD’s, Intel’s and Microsoft’s CEOs (Chief Execution Officers):
But it is also an opportunity and challenge for individuals and institutions
to catch up with the progress and make benefit of it.
Conclusions -3
*

## Slide 127
6. References
Notes: 127

## Slide 128
[1]: Bártfai D., Merre felé tartanak a hardverek?, Aug. 22-24 2007
6. References (1)
[3]: AMD 2013 Mobility APU Introduction, May 22 2013,
http://www.slideshare.net/AMD/amd-2013-mobility-apu-introduction-deck-final-for-lp
[4]: Frommer D., CHART OF THE DAY: Smartphone Sales To Beat PC Sales By 2011,
Business Insider, Aug. 21 2009, http://www.businessinsider.com/chart-of-the-day-
smartphone-sales-to-beat-pc-sales-by-2011-2009-8
[5]: Wikipedia, BlackBerry Pearl, http://en.wikipedia.org/wiki/BlackBerry_Pearl
[6]: Wikipedia, Android (operating system),
http://en.wikipedia.org/wiki/Android_%28operating_system%29
[2]: Smith S.L., Intel Strategy & Technology Update, Barclays Capital Global Technology Conf.,
Dec. 2011, http://files.shareholder.com/downloads/INTC/1576180143x0x526852/c9868a3a-
494e-4506-bcc6-a631aca1fd75/Steve%20Smith%20Barclays%20Dec%202011.pdf
[7]: Ciufo C.A., Tizen OS for Smartphones – Intel’s Biggest Bet Yet, Jan. 4 2013,
http://eecatalog.com/caciufo/2013/01/04/samsung-hedges-apple-google-bets-with-intels-
html5-based-tizen/
[8]: Introduction of the Next Generation Intel Atom Processor, Oak Trail Z670, 4/2011,
http://newsroom.intel.com/docs/DOC-1976
[9]: Apple Maintains 48 Percent Share of Global Branded Tablet Shipments in Q1 2013,
Strategy Analytics, April 25 2013, Boston,
http://www.strategyanalytics.com/default.aspx?mod=pressreleaseviewer&a0=5351
6. References

## Slide 129
[10]: Goto H., ARM Cortex – A Family Architecture, 2010,
http://pc.watch.impress.co.jp/video/pcw/docs/423/409/p1.pdf
6. References (2)
[12]: Wikipedia, iPad, http://en.wikipedia.org/wiki/IPad
[11]: Eul H., Bell M., Mobile at Intel, Investor Meeting 2012,
http://www.cnx-software.com/pdf/Intel_2012/2012_Intel_Investor_Meeting_Eul_Bell.pdf
[13]: Tablet Platforms with Next Generation Intel Atom Processor and Microsoft Windows 8,
IDF 2012
[14]: The $15.3 Billion Server Market – Surprisingly Buoyant In Q1 2012, IT Candor, July 3 2012,
http://www.itcandor.com/server-q112/
[15]: Shah A., Intel Loses Laptop Chip Market Share to AMD in Q3, PC World, Nov. 3 2011,
http://www.pcworld.com/article/243114/intel_loses_laptop_chip_market_share_to_amd_
in_q3.html
[16]: Perry D., AMD Steals Market Share From Intel, Tom’s Hardware, March 16 2012,
http://www.tomshardware.com/news/amd-intel-cpu-processor,15041.html
[17]: Shilov A., AMD Shows Off Opteron "Interlagos" Again: No Performance Benchmarks,
No Design Wins, No Launch Date Announced, Xbit Labs, Aug. 3 2011,
http://www.xbitlabs.com/news/cpu/display/20110803103016_AMD_Shows_Off_Opteron_
Interlagos_Again_No_Performance_Benchmarks_No_Design_Wins_No_Launch_Date_
Announced.html
[18]: Arthur C., PC business still waning as Microsoft's Windows 8 fails to lift it, 11 July 2013,
http://www.theguardian.com/technology/2013/jul/11/pc-business-microsoft-windows-8

## Slide 130
6. References (3)
[19]: Golson J., Steve Jobs Envisioned the iPad in 1983, MacRumors, Oct. 2, 2012,
http://www.macrumors.com/2012/10/02/steve-jobs-envisioned-the-ipad-in-1983/
[20]: Yarow J., Steve Ballmer's Biggest Mistakes As CEO Of Microsoft, Business Insider, Aug. 27
2013,
http://www.businessinsider.com/steve-ballmers-most-epic-mistakes-as-ceo-of-microsoft-
2013-8?op=1
[21]: Arora, P., Microsoft Is Not Killing The Surface RT Lineup? Seeking Alpha, Aug. 25 2014,
http://www.macrumors.com/2012/10/02/steve-jobs-envisioned-the-ipad-in-1983/
[22]: Surface Pro 3 Fact sheet May 2014, Microsoft,
http://www.microsoft.com/global/eu/PublishingImages/Surfacepro3texhspecs.pdf
[23]: Microsoft Surface Pro, NDTV Gadget, May 2014,
http://gadgets.ndtv.com/microsoft-surface-pro-3-1611
[24]: Guenette S., Nearly $2 Billion In The Hole, Microsoft Continues To Dive Deeper Into Tablets,
Seeking Alpha, Aug. 8, 2014,
http://seekingalpha.com/article/2402725-nearly-2-billion-in-the-hole-microsoft-continues
-to-dive-deeper-into-tablets
[25]: Deskovich V., Microsoft: A Monopoly No More? Seeking Alpha, Jul. 11, 2014
http://seekingalpha.com/article/2309835-microsoft-a-monopoly-no-more
[26]: Gill R., Intel’s Core i5-655K & Core i7-875K: Overclocked and Analyzed, AnandTech,
May 28 2010, http://www.anandtech.com/show/3742/intels-core-i5655k-core-i7875k-
overclocked-and-analysed-/2
[27]: Shimpi A. L., AMD Beema/Mullins Architecture & Performance Preview, AnandTech,
April 29, 2014, http://www.anandtech.com/show/7974/amd-beema-mullins-architecture-
a10-micro-6700t-performance-preview

## Slide 131
[28]: Wilson S., & Wigginton C., Making open innovation work in mobile - Insights from the
semiconductor industry, Deloitte University Press, July 24v2013,
http://dupress.com/articles/making-open-innovation-work-in-mobile/
[30]: Arora P., Wait, Microsoft Is Not Killing The Surface RT Lineup? Seeking Alpha, Aug. 25, 2014,
http://seekingalpha.com/article/2447735-wait-microsoft-is-not-killing-the-surface-rt-lineup
[31]: Hodgins K., Apple Maintains Narrowing Lead in Tablet Market Share, MacRumors, May 1,
http://www.macrumors.com/2014/05/01/apple-tablet-market-share-1q14
[32]: Arora P., Wait, Microsoft Is Not Killing The Surface RT Lineup? Seeking Alpha, Aug. 25, 2014,
http://seekingalpha.com/article/2447735-wait-microsoft-is-not-killing-the-surface-rt-lineup
[33]: Eul H., & Bell M., Mobile at Intel, Investor Meeting 2012, Intel,
http://www.cnx-software.com/pdf/Intel_2012/2012_Intel_Investor_Meeting_Eul_Bell.pdf
[34]: Qualcomm dominates smartphone chip and baseband, tablet processor markets, Mobile
Europe, February 17 2014
http://www.mobileeurope.co.uk/Press-Wire/qualcomm-dominates-smartphone-chip-and
-baseband-tablet-processor-markets
[35]: Gartner Says Worldwide Tablet Sales Grew 68 Percent in 2013, With Android Capturing 62
Percent of the Market, Gartner, Newsroom, March 3, 2014,
http://www.gartner.com/newsroom/id/2674215
[36]: Trefis Team, Why Intel Can Gain Additional Share In The Mobile Market, Forbes, 5/09/2014
http://www.forbes.com/sites/greatspeculations/2014/05/09/why-intel-can-gain-additional-
share-in-the-mobile-market
6. References (4)

## Slide 132
[37]: Meeker M., Devitt S., Vu L., Internet Trends, CM Summit, Morgan Stanley, New York,
June 7, 2010, http://demo.tizra.com/Morgan-Stanley-Internet-Trends-June-7-2010/3
[38]: Hardy E., BlackBerry Pearl 8100 Review, Brighthand, November 15 2006,
http://www.brighthand.com/phonereview/blackberry-pearl-8100-review/
[39]: Nokia 7650, Wikipedia, http://en.wikipedia.org/wiki/Nokia_7650
[40]: Bokil-Paranjape S., Worldwide smartphone sales hit 267 million in Q1 2014: Trend Force,
Phonearena, April 18 2014, http://www.fonearena.com/blog/101450/worldwide-
smartphone-sales-hit-267-million-in-q1-2014-trend-force.html
[41]: Grifiths H., How the ubiquity of today’s smartphones make an ideal platform for delivering
campus-based services, Ombiel, 2010,
http://www.rms-inc.com/files/datasheets/Ombiel_Whitepaper.pdf
[42]: Richter F., Android To Retain Big Lead In Maturing Smartphone Market, Statista, March 4
2014, http://www.statista.com/chart/1961/smartphone-market-share-2014
[43]: Smartphone Apps Processor Revenue Reached $4.7 Billion in Q1 2014 says Strategy
Analytics, Strategy Analytics, July 14 2014,
http://www.strategyanalytics.com/default.aspx?mod=pressreleaseviewer&a0=5543
[44]: Klug B. & Shimpi A. L., Qualcomm's New Snapdragon S4: MSM8960 & Krait Architecture
Explored, AnandTech, Oct. 7 2011, http://www.anandtech.com/show/4940/qualcomm-
new-snapdragon-s4-msm8960-krait-architecture
[45]: Lomas N., Report: Intel Gained Just 0.2% Of Smartphone Chip Market In 1H As Qualcomm
Milked LTE Lead, Tech Crunch, Oct. 5 2012, http://techcrunch.com/2012/10/05/report-
intel-gained-just-0-2-of-smartphone-chip-market-in-1h-as-qualcomm-milked-lte-lead
6. References (5)

## Slide 133
[46]: Klug B., Intel XMM7160 LTE Modem Demonstrated on Live Network, AnandTech, Sept. 11
2013, http://www.anandtech.com/show/7321/intel-xmm7160-lte-modem-demonstrated-
on-live-network
6. References (6)
[47]: Bocha, Apple iPhone megateszt, Mobilarena, 2007-07-23,
http://mobilarena.hu/teszt/apple_iphone_megateszt_a_bunbeeses_almaja/bevezeto.html
[48]: Shimpi A.L., Apple's Cyclone Microarchitecture Detailed, AnandTech, March 31 2014,
http://www.anandtech.com/show/7910/apples-cyclone-microarchitecture-detailed
[49]: Dilger D.E., Apple's new A8X powered iPad Air 2 smokes new Android tablets, including
Nvidia's Tegra K1 Shield Tablet [u], Apple Insider, Oct. 21 2014,
http://appleinsider.com/articles/14/10/21/apples-new-a8x-powered-ipad-air-2-smokes-
new-android-tablets-including-nvidias-tegra-k1
[50]: Dilger D.E., Apple Inc. A8X iPad chip causing big problems for Intel, Qualcomm, Samsung
and Nvidia, Apple Insider, Nov. 14 2014,
http://appleinsider.com/articles/14/11/15/apple-inc-a8x-ipad-chip-causing-big-problems-
for-intel-qualcomm-samsung-and-nvidia
[51]: De Gelas J., The Intel Xeon E7-8800 v3 Review: The POWER8 Killer?, AnandTech,
May 8, 2015, http://www.anandtech.com/show/9193/the-xeon-e78800-v3-review
[52]: Global PC shipments from 1st quarter 2009 to 2nd quarter 2015, by vendor (in million units),
Statista, http://www.statista.com/statistics/263393/global-pc-shipments-since-1st-
quarter-2009-by-vendor/

## Slide 134
[53]: Gartner Says Worldwide Smartphone Sales Recorded Slowest Growth Rate Since 2013,
Gartner, Newsroom, Aug. 20 2015, http://www.gartner.com/newsroom/id/3115517
6. References (7)
[54]: Leswing K., Asus Zenfone 2 Preview: Intel's Best Chance In Years To Break Into
Smartphones, International Business Time, May 19 2015,
http://www.ibtimes.com/asus-zenfone-2-preview-intels-best-chance-years-break-
smartphones-1929726
[55]: Richter F., Tablets to Outsell PCs Worldwide by 2015, Statista, Febr. 28 2014,
http://www.statista.com/chart/1138/tablet-and-pc-shipment-forecast/
[56]: Dilger D. E., After losing Apple's iPad business, Intel has bled $7 billion while heavily
subsidizing cheap x86 Atom Android tablets, Appleinsider, November 16, 2014,
http://appleinsider.com/articles/14/11/16/after-losing-apples-ipad-business-intel-has-
bled-7-billion-while-heavily-subsidizing-cheap-x86-atom-android-tablets
[57]: Smartphone and tablet processor market share in 2014, May 7 2015
http://mobilesemi.blogspot.hu/2015/05/smartphone-and-tablet-processor-market.html
[58]: Cutress I., The Intel Skylake Mobile and Desktop Launch, with Architecture Analysis,
AnandTech, Sept. 1 2015, http://www.anandtech.com/show/9582/intel-skylake-mobile-
desktop-launch-architecture-analysis
[59]: Klug B., The State of Qualcomm's Modems - WTR1605 and MDM9x25, AnandTech,
Jan. 4 2013, http://www.anandtech.com/print/6541/the-state-of-qualcomms-modems-
wtr1605-and-mdm9x25
[60]: iPhone 6 Plus Teardown, iFixit,
https://www.ifixit.com/Teardown/iPhone+6+Plus+Teardown/29206

## Slide 135
[61]: Ho J., Qualcomm Details Hexagon 680 DSP in Snapdragon 820: Accelerated Imaging,
AnandTech, August 24, 2015, http://www.anandtech.com/print/9552/qualcomm-details-
hexagon-680-dsp-in-snapdragon-820-accelerated-imaging
6. References (8)
[62]: QSC6055/QSC6065/QSC6075/QSC6085 Hardware Training, Introductions and Device
Overview, 80-VC881-21 Rev. A, April 2007,
http://www.droid-developers.org/images/3/3c/Qsc6085-overview.pdf
[63]: James D., Inside Today’s Systems & Chips: A Survey of the Past Year, Chipworks, 2013,
http://theconfab.com/wp-content/uploads/2014/dick_james_confab14.pdf
[64]: Global unit sales of current generation video game consoles from 2008 to 2014 (in million
units), Statista, http://www.statista.com/statistics/276768/global-unit-sales-of-video-
game-consoles/
[65]: CPU Benchmarks, Passmark Software, 10th june 2016,
http://www.cpubenchmark.net/market_share.html
[66]: Anchorite, AMD Is A Threat To Intel's X86 Market Share, Not Vice Versa, Seeking Alpha,
Jun. 10, 2016 ,
http://seekingalpha.com/article/3981352-amd-threat-intels-x86-market-share-vice-versa?
auth_param=djq9a:1blm8ut:579a4c85ebfd66607461f023a383c45c
[67]: Gartner Says Five of Top 10 Worldwide Mobile Phone Vendors Increased Sales in
Second Quarter of 2016, Gartner, Aug. 19, 2016,
http://www.gartner.com/newsroom/id/3415117
[68]: Jan C.-H., RF CMOS Technology Scaling in High-k/Metal Gate Era for RF SoC (System-on-
Chip) Applications, IEDM ’10, San Francisco 2010,
http://www.intel.com.br/content/dam/doc/technology-brief/32nm-soc-with-rf-cmos-
technology-presentation.pdf

## Slide 136: 6. References (9)
[69]: Smartphone Vendor Market Share, 2017 Q1, IDC ,
https://www.idc.com/promo/smartphone-market-share/vendor
[70]: Smartphone OS Market Share, 2017 Q1, IDC,
https://www.idc.com/promo/smartphone-market-share/os
[71]: Apple Tied with MediaTek for the #2 Spot in the Global Smartphone Applications Processor
Market, Patently Apple, 2107,
http://www.patentlyapple.com/patently-apple/2017/10/apple-tied-with-mediatek-for-the-
2-spot-in-the-global-smartphone-applications-processor-market.html
[72]: Kay A. C., (Xerox Palo Alto Research Center) A Personal Computer for Children of All Ages,
Proceedings of the ACM National Conference, Boston Aug. 1972 Vol. 1 Article No. 1.
[73]: Gruener W., Did Steve Jobs Steal The iPad? Genius Inventor Alan Kay Reveals All, Tom's
Hardware, April 17, 2010,
http://www.tomshardware.com/news/alan-kay-steve-jobs-ipad-iphone,10209.html
[74]: Triggs R., Intel is losing billions on mobile development, Android Authority, April 16, 2014,
https://www.androidauthority.com/intel-losing-billions-on-mobile-369148/
[75]: Shipment forecast of laptops, desktop PCs and tablets worldwide from 2010 to 2021
(in million units), Statista,
https://www.statista.com/statistics/272595/global-shipments-forecast-for-tablets-laptops
-and-desktop-pcs/
[76]: Worldwide Tablet Shipments Decline More Than 12% in Second Quarter as the Market
Shifts Its Focus Toward Productivity, IDC, 01 Aug 2016,
https://www.idc.com/getdoc.jsp?containerId=prUS41632416

## Slide 137: 6. References (10)
[77]: Dilger D. E.: IDC offers a rosy forecast for Microsoft Surface, reminiscent of its 2012
Windows Phone outlook, Appleinsider, Dec. 02, 2015,
http://appleinsider.com/articles/15/12/02/idc-offers-a-rosy-forecast-for-microsoft-surface-
reminiscent-of-its-2012-windows-phone-outlook
[78]: Jourdan S., Broadwell Microarchitecture Disclosures, Intel, Aug. 11, 2014,
http://download.intel.com/newsroom/kits/14nm/pdfs/Intel_14nm_New_uArch.pdf
[79]: iPad Air 2 Teardown, iFixit,
https://www.ifixit.com/Teardown/iPad+Air+2+Teardown/30592
[80]: Shimpi A. L., The ARM vs x86 Wars have Begun: In-Depth Power Analysis of Atom,
Krait C Cortex A15, AnandTech, Jan. 4, 2013,
https://www.anandtech.com/show/6536/arm-vs-x86-the-real-showdown
[81]: Nguyen H., NVIDIA Definitely “Not Interested” In Building Smartphones SoCs, Ubrergizmo,
06/04/2016,
http://www.ubergizmo.com/2016/06/nvidia-not-interested-smartphones-soc/
[82]: Smith R. and Cutress I., Intel's Changing Future: Smartphone SoCs Broxton & Sophia
Officially Cancelled, AnandTech, April 29, 2016,
https://www.anandtech.com/show/10288/intel-broxton-sofia-smartphone-socs-cancelled
[83]: Hruska J., How Intel lost the mobile market, part 2: the rise and neglect of Atom,
Extreme Tech, May 4, 2016,
https://www.extremetech.com/computing/227816-how-intel-lost-the-mobile-market-part-
2-the-rise-and-neglect-of-atom
[84]: Surface Pro (2017),
https://en.wikipedia.org/wiki/Surface_Pro_(2017)

## Slide 138: 6. References (11)
[85]: Microsoft Lumia,
https://en.wikipedia.org/wiki/Microsoft_Lumia
[86]: Warren T., Microsoft just hinted it's the end of Lumia phones, The Verge, Mai 18, 2016,
https://www.theverge.com/2016/5/18/11699766/microsoft-lumia-phone-brand
[87]: Tyson M., Leaked slides show AMD desktop and mobility roadmaps for 2016, Hexus,
April 30, 2015,
http://hexus.net/tech/news/cpu/82813-leaked-slides-show-amd-desktop-mobility-
roadmaps-2016/
[88]: Tablet operating systems' market share worldwide from 2013 to 2020, Statista, 2017,
https://www.statista.com/statistics/272446/global-market-share-held-by-tablet-operating-
systems/
[89]: Number of smartphones sold to end users worldwide from 2007 to 2016 (in million units),
Statista, 2017
https://www.statista.com/statistics/263437/global-smartphone-sales-to-end-users-since-
2007/
[90]: Kahn O., Valentine B.: Intel Next Generation Microarchitecture Codename Sandy Bridge:
New Processor Innovations, IDF 2010
[91]: Desktop Windows Version Market Share Worldwide, Statcounter, Nov. 2016 - Nov. 2017,
http://gs.statcounter.com/os-version-market-share/windows/desktop/worldwide
[92]: Qualcomm Announces Flagship Companies to Build Windows 10 PCs Powered by
Snapdragon, Qualcomm, Press Release, May 31 2017
https://www.qualcomm.com/news/releases/2017/05/31/qualcomm-announces-flagship-
companies-build-windows-10-pcs-powered

## Slide 139: [93]
[93]: Warren T., Microsoft is bringing Windows desktop apps to mobile ARM processors,
The Verge, Dec. 7, 2016,
https://www.theverge.com/2016/12/7/13866936/microsoft-windows-10-arm-desktop-
apps-support-qualcomm