## Slide 1
Dezső Sima
© Dezső Sima 2018
(v3.2)
ARM’s processor lines
November 2018

## Slide 2
ARM’s processor lines
1. Evolution of ARM
2. Evolution of the ARM ISA
4. Evolution of the Cortex-A series
ARMv7/v8.0 ISA-based models
3. Overview of ARM’s processor families
6. Cortex-A models based on the ARMv8.2 ISA
7. Overview of ARM’s Mali graphics series
5. Cortex-A models based on the ARMv8.0 ISA
8. References
Notes: 2

## Slide 3: ARM’s processor lines
Note
In the Lecture (Fall 2018) only the following Sections will be discussed:
Section 1: Evolution of ARM
From Section 2: Evolution of the ARM ISA
xx 2.1: Overview
From Section 2.2: ISA extensions introduced to enhance compute capabilities
2.2.1: Overview
Section 3.4: Processors implementing the ARM v7 - ARM v8 ISA
Section 4: Evolution of the Cortex-A series models that are based on the
ARMv7/v8.0 ISA
Section 6: Cortex-A models based on the ARMv8.2 ISA

## Slide 4
1. Evolution of ARM

## Slide 5: 1. Evolution of ARM (1)
The company
1. Evolution of ARM
plc: public limited company (a.m. kft)
ARM (ARM Holdings plc) is a British multinational semiconductor company with
its head office in Cambridge, acquired by Softbank (Japan) in 2016.
ARM processors for the embedded, mobile and server market,
mobile GPUs (termed as Mali GPUs) as well as
design tools (development studios etc.),
their IP (Intellectual Property) including their ISA but does not fabricate
semiconductors.
intellectual property: a.m. szellemi tulajdon
*
designs low power
and licences

## Slide 6: 1. Evolution of ARM (2)
Graphic IP | Other IP | Tools
ARM Mali™-G71 Mali-DP550 (Display processor) Mali-V550 (Video Processor) | ARM CoreLink™ CCI-550 (Cache Coherent Interconnect) CoreLink GIC-500 (Interrupt Controller) CoreLink MMU-500 (System Memory Management Unit) CoreLink TZC-400 (ARM TrustZone® Controller) CoreLink DMC-500/DMC-520 (Dynamic Memory Controller) ARM CoreSight™ SoC-400 (Debug and Trace) ARM POP™ (Physical IP) | ARM DS-5 Development Studio Fixed Virtual Platforms ARM Versatile™ Express ARM Compiler 6 ARM Fast Models
Example: ARM's IP offer relating the Cortex-A73 processor [89]

## Slide 7: 1. Evolution of ARM (3)
ARM's business model [117]

## Slide 8: 1. Evolution of ARM (4)
Example for the range of configurability of a processor [90]
Configuration options of the Cortex-A35 ranging from mobile to deeply embedded

## Slide 9: 1. Evolution of ARM (5)
Semi custom design
Full synthesizable design
Approaches to circuit design
Full custom design
Hand layout of the
entire circuit
Automated layout of the
entire circuit
Simple scaling, e.g.
from 28 nm to 16 nm
The design will be subdivided into
functional units and further on into blocks
and the appropriate implementation technique
(hand layout, structured layout or automated layout)
is chosen for each.
Power/performance
optimized
Implementation time
optimized
Evolution of the approaches used to circuit design -1 [1]
Trend

## Slide 10: 1. Evolution of ARM (6)
Over time more and more advanced standard cell libraries were developed that
have a large variety of design options, e.g. cell types or drive strengths, which
lessens the need for custom design.
Recently, automated design tools are typically used for processor design.
ARM's processor designs before the Cortex-A9 were partly hand layouts and
partly automated layouts.
ARM’s first fully synthesizable design was the Cortex-A9 processor
(announced in 2007).
Evolution of the approaches used to circuit design -2 [1]

## Slide 11: 1. Evolution of ARM (7)
4xA53 2.0+
4xA57 1.55
2xKryo 2.15+
2xKryo 1.59
4xKryo 280 2.45+
4xKryo 280 1.9
(Full synthesizable design)
20 nm
(2015)
14 nm
(2015)
10 nm
(2016)
Design approaches used by Qualcomm to develop recent processors [116]

## Slide 12: 1. Evolution of ARM (8)
ARM designs dominate recently the embedded and the mobile market
(including smartphones and tablets).
As of 2014 more than 50 billion ARM based processors have been produced
in total, up from 10 billion in 2008 [59], [19], as indicated in the next Figure.
Dominance of AMD designs in the embedded and mobile market
(including smartphones and tablets)

## Slide 13: 1. Evolution of ARM (9)
Total number of ARM based chips shipped [19]
Keil: Software development tool for embedded processors
Linaro: Nonprofit company, established by ARM, Freescale, IBM, Samsung, ST-Ericsson and TI
to support open source software developers using Linux on SoCs.
SBSA: Server Base System Architecture, a standardized server platform for 64-bit ARM processors.

## Slide 14: 1. Evolution of ARM (10)
ARM’s parent company is Acorn Computers (UK).
Acorn Computers started their Acorn RISC Machine project in October 1983
(two years after the introduction of the IBM PC) to develop an own powerful
processor for a line of business computers.
The acronym ARM was coined originally at this time (1983) from the designation
Acorn RISC Machine.
In 1990 the company Advanced RISC Machines Ltd. (ARM Ltd.) was founded as a
joint venture of Acorn Computers, Apple Computers and VLSI Technology.
Accordingly, also the interpretation of ARM was changed to “Advanced RISC
Machines”.
Historical remarks [60], [61] -1

## Slide 15: 1. Evolution of ARM (11)
Figure: The headquarters of ARM Ltd. about 1990 [62]
Historical remarks -2

## Slide 16: 1. Evolution of ARM (12)
Finally, in 1998 the company went to the stock exchange and its name was changed
to ARM Holdings plc, to its current designation.
Historical remarks -3

## Slide 17: 1. Evolution of ARM (13)
Historical remarks -4
Figure: ARM's recent headquarter in Cambridge (UK) [78]

## Slide 18: 1. Evolution of ARM (14)
Acquisition of ARM by Softbank (Japan)
Announced in 07/2016
Completed in 09/2016
Price: 31 bUSD (ARM's revenues in 2015 ≈ 1.5 bUSD)

## Slide 19
2. Evolution of the ARM ISA
2.1 Overview
2.2 ISA extensions introduced to enhance compute capabilities
2.3 ISA extensions introduced to reduce the code size
2.4 ISA extensions introduced to enhance security
(Only Section 2.1 and 2.2.1 will be discussed)

## Slide 20
2.1 Overview

## Slide 21: 2.1 Overview (1)
2.1 Overview
There are eight ARM ISA versions, designated as ARMv1 to ARMv8.
These are described in the related Architecture Reference Manuals.
The earliest versions (ARMv1 and ARMv2) provided an address range of only
26 bits, the first ISA version with 32 bit address range was the ARMv3.
Accordingly, we consider the ISA version ARMv3 as ARM’s basic ISA and discuss
its evolution subsequently.
*

## Slide 22: 2.1 Overview (2)
Example: Half page of the ARMv8 Architecture Reference Manual []
(1/2 from 6354)

## Slide 23: 2.1 Overview (3)
Key features of ARM’s basic ISA
It is a 32-bit RISC ISA capable to process basically 32-bit scalar FX or logical data.
The ISA has 16 32-bit registers, called the core registers.
13 out of them are used as general purpose registers (GPRs), the remaining three
are dedicated registers, as shown below.
Stack pointer
Link register
PC
Figure: The core registers of the ARM ISA (in the ISA versions ARMv3-ARMv7) [63]
*

## Slide 24: 2.1 Overview (4)
Main extensions introduced in ARM’s basic ISA (simplified) -1
ISA extensions
to enhance
compute capabilities
ARM’s ISA extensions
ISA extensions
to speed up
the execution of bytecodes
ISA extensions
to enhance
security
ISA extensions
to reduce
code size
Section 2.2
Section 2.3
Section 2.4
Section 2.5
*

## Slide 25: 2.1 Overview (5)
ARMv4
ARMv5
ARMv6
ARMv8-A
ARMv7-A/R
Jazelle
(Jazelle DBX)
VFPv1/2
Thumb
(ARMv4T)
SIMD
TrustZone
Thumb-2
(ARMv6T2)
Adv. SIMD1
(NEON)
VFPv3/v42
Crypto-graphy ext.
Jazelle
(ex. by SW)
Jazelle RCT3
(ThumbEE)
ARM710T
(~1995)
ARM926
(2001)
ARM1176
(2004)
Cortex-A5 - A15
(2005)
Cortex-A53/A57
(2014)
Examples
To enhance
security
To speed up
the execution
of bytecodes
To reduce
code size
SVE4
To enhance
compute
capabilities
AArch32
AArch64
Main extensions introduced in ARM’s basic ISA (simplified) -2 (Based on [64])
Remarks: See on the next slide.
Adv. SIMD and FP
SIMD
and FP

## Slide 26: 2.1 Overview (6)
1The Advanced SIMD architecture extension is commonly referred to as the
NEON technology.
The VFP subset became depricated in the ARMv8 ISA.
3Jazelle-RTC (ThumbEE) became depricated in ARMv7 Issue C in 10/2011.
4The SVE (Scalable Vector Extension) subset became introduced in the
ARMv8 ISA only in 2016.
Remarks

## Slide 27
2.2 ISA extensions introduced to enhance compute capabilities
2.2.1 Overview
2.2.2 The GPR register set based SIMD extension
2.2.3 Secondary register set based VFP and NEON extensions
2.2.4 The SVE register set based SVE extension
Only Section 2.2.1 will be discussed.

## Slide 28
2.2.1 Overview

## Slide 29: 2.2.1 Overview (1)
2.2 ISA extensions introduced to enhance compute capabilities
2.2.1 Overview
ISA extensions
to enhance
compute capabilities
ARM’s ISA extensions
ISA extensions
to speed up
the execution of bytecodes
ISA extensions
to enhance
security
ISA extensions
to reduce
code size
Section 2.2
Section 2.3
Section 2.4
Section 2.5

## Slide 30: 2.2.1 Overview (2)
Remarks: See on the slide 2.1 Overview (5).
Overview of the ISA extensions introduced to enhance compute capabilities
ARMv4
ARMv5
ARMv6
ARMv8-A
ARMv7-A/R
Jazelle
(Jazelle DBX)
VFPv1/2
Thumb
(ARMv4T)
SIMD
TrustZone
Thumb-2
(ARMv6T2)
Adv. SIMD1
(NEON)
VFPv3/v42
Crypto-graphy ext.
Jazelle
(ex. by SW)
Jazelle RCT3
(ThumbEE)
ARM710T
(~1995)
ARM926
(2001)
ARM1176
(2004)
Cortex-A5 - A15
(2005)
Cortex-A53/A57
(2012)
Examples
To enhance
security
To speed up
the execution
of bytecodes
To reduce
code size
SVE4
To enhance
compute
capabilities
AArch32
AArch64
Adv. SIMD and FP
SIMD
and FP

## Slide 31: 2.2.1 Overview (3)
Section 2.2.2
Section 2.2.3
Section 2.2.4
It supports
FX-SIMD operations
It supports
FX/FP scalar and SIMD operations
It supports
FX/FP SIMD operations
on long vector data
ISA extensions introduced to enhance compute capabilities
ARMv6
ARMv5
ARMv8.2
SVE: Scalable Vector Extension
*
The GPR register set based
SIMD extension
A secondary register set added
with FP and SIMD extensions
An SVE register set added
with SIMD extensions
ARM’s ISA extensions to enhance compute capabilities

## Slide 32: 2.2.1 Overview (4)
It supports
FX-SIMD operations
It supports
FX/FP scalar and SIMD operations
It supports
FX/FP SIMD operations
on long vector data
ISA extensions introduced to enhance compute capabilities
Section 2.2.2
Section 2.2.3
Section 2.2.4
ARMv6
ARMv5
ARMv8.2
The GPR register set based
SIMD extension
A secondary register set added
with FP and SIMD extensions
An SVE register set added
with SIMD extensions
ARM’s ISA extensions to enhance compute capabilities

## Slide 33: 2.2.1 Overview (5)
ARM ISA |  | Name of the extensions | Basic arch. |  | GPR-based FX-SIMD data type extension | Secondary register set based extensions |  | 
 |  |  | GPRs | Data type |  | Available reg. set | Scalar data types | Vector data types
Name |  |  |  |  |  |  |  | 
ARMv1 | 1985 |  | n.a. | FX32 |  |  |  | 
ARMv2 | 1989 |  | n.a. |  |  |  |  | 
ARMv3 | 1991 |  | 13x32 |  |  |  |  | 
ARMv4 | 1996 |  |  |  |  |  |  | 
ARMv5 | Year | VFP(v1)1 |  |  |  | FP register set 32x32/16x64 | FP 32/64 | FP 32/64 Serially ex.
 |  | VFP21 |  |  |  |  |  | 
ARMv6 |  | SIMD |  |  | 32-bit wide FX8/16 |  |  | 
ARMv7 | 2005 | VFPv32 |  |  |  | Adv. SIMD and FP register set 32x64 or 16X128 | +FP 164 | FP 164/32/64 Serially executed
 |  | VFPv42,3,4 |  |  |  |  | + FMA | 
 |  | Adv. SIMD (NEON)4,5 |  |  |  | 32x64 or16x128 |  | 64/128-bit wide FX 8/16/32/64 FP 165/32/64 +FMA5
ARMv8 | 2012 | AArch32 | 31x64 | FX32/64 | 32-bit wide FX8/16 | 32x64 or 16x128 | FP 164/32/64 | As for ARMv7 Adv. SIMD
 |  | AArch64 |  |  | 32/64-bit wide FX8/16/32 | SIMD and FP register set 32x128 | FX 8/…/64 FP 164/32/64 | As for ARMv7 Adv. SIMD
ISA extensions introduced to enhance compute capabilities (until 2012)

## Slide 34: 2.2.1 Overview (6)
1VFPv2 vs. VFP(v1): VFPv2 adds some enhancements and modifications to VFPv1
Remarks
2VFPv3/v4 and advanced SIMD register space:
Certain processors implement only 16 64-bit wide registers with the option to use
this register space as 32 32-wide registers.
3VFP4 is implemented on certain ARMv7 processors.
It adds FMA (Fused Multiply Accumulate) instructons to the VFPv3 instructon set.
4FP16 supports only data conversion between FP16 and FP32/FP64.
5In the Advanced SIMD (NEON) extension FP16 is supported only if VFP3/VFP4
is implemented respectively, FMA if VFP4 is implemented.

## Slide 35: 2.2.1 Overview (7)
32
31
ARMv3
Previously 26 bitwide)
32
13
ARMv7
The GPR register set based SIMD extension introduced in the ARMv6 ISA
GPR register set
64
31
ARMv8
(AArch64)
32
13
...
...
ARMv6
Scalar data
FX32
SIMD
extension
32-bit wide FX-SIMD FX8/16 operations
Basic ISA
SIMD data
ARMv8
(Aarch32)
32-bit data
64-bit data
32
13
FX64
FX32

## Slide 36: 2.2.1 Overview (8)
Dedicated use
Dedicated use
Stack pointer
Link register
PC
32-bit wide
32-bit wide
64-bit wide
GPRs in the ARMv3-ARMv7 and the
ARMv8 AArch32 execution mode
32-bit access
64-bit access
GPRs in the ARMv8 AArch64 execution mode
R0
R1
R2
.
.
.
R12
R13(SP)
R14(LR)
R15(PC)
X0
X1
X2
.
.
.
X12
X13
X14
.
.
.
X30
X31
X3
W0
W1
W2
.
.
.
W12
W13
W14
.
.
.
W30
W31
W3
Extension of the GPR register set available in the ARMv8 ISA 63], [66]
The ARMv8 ISA expanded the number of GPRs as seen in the Figure below.
*

## Slide 37: 2.2.1 Overview (8b)
32
31
ARMv3
Previously 26 bitwide)
32
13
ARMv7
The GPR register set based SIMD extension introduced in the ARMv8 ISA
GPR register set
64
31
ARMv8
(AArch64)
32
13
...
...
ARMv6
Scalar data
FX32
SIMD
extension
32-bit wide FX-SIMD FX8/16 operations
Basic ISA
SIMD data
32-bit wide FX-SIMD FX8/16 operations
SIMD data
64-bit wide FX-SIMD
FX8/16/32 operations
SIMD data
ARMv8
(Aarch32)
32-bit data
64-bit data
32
13
FX64
FX32

## Slide 38: 2.2.1 Overview (9)
It supports
FX-SIMD operations
It supports
FX/FP scalar and SIMD operations
It supports
FX/FP SIMD operations
on long vector data
Secondary register set based FP and SIMD extensions -1
Section 2.2.2
Section 2.2.3
Section 2.2.4
ARMv6
ARMv5
ARMv8.2
The GPR register set based
SIMD extension
A secondary register set added
with FP and SIMD extensions
An SVE register set added
with SIMD extensions
ARM’s ISA extensions to enhance compute capabilities

## Slide 39: 2.2.1 Overview (10)
ARM ISA |  | Name of the extensions | Basic arch. |  | GPR-based FX-SIMD data type extension | Secondary register set based extensions |  | 
 |  |  | GPRs | Data type |  | Available reg. set | Scalar data types | Vector data types
Name |  |  |  |  |  |  |  | 
ARMv1 | 1985 |  | n.a. | FX32 |  |  |  | 
ARMv2 | 1989 |  | n.a. |  |  |  |  | 
ARMv3 | 1991 |  | 13x32 |  |  |  |  | 
ARMv4 | 1996 |  |  |  |  |  |  | 
ARMv5 | Year | VFP(v1)1 |  |  |  | FP register set 32x32/16x64 | FP 32/64 | FP 32/64 Serially ex.
 |  | VFP21 |  |  |  |  |  | 
ARMv6 |  | SIMD |  |  | 32-bit wide FX8/16 |  |  | 
ARMv7 | 2005 | VFPv32 |  |  |  | Adv. SIMD and FP register set 32x64 or 16X128 | +FP 164 | FP 164/32/64 Serially executed
 |  | VFPv42,3,4 |  |  |  |  | + FMA | 
 |  | Adv. SIMD (NEON)4,5 |  |  |  | 32x64 or16x128 |  | 64/128-bit wide FX 8/16/32/64 FP 165/32/64 +FMA5
ARMv8 | 2012 | AArch32 | 31x64 | FX32/64 | 32-bit wide FX8/16 | 32x64 or 16x128 | FP 164/32/64 | As for ARMv7 Adv. SIMD
 |  | AArch64 |  |  | 64-bit wide FX8/16/32 | SIMD and FP register set 32x128 | FX 8/…/64 FP 164/32/64 | As for ARMv7 Adv. SIMD
Secondary register set based FP and SIMD extensions -2

## Slide 40: 2.2.1 Overview (11)
ARMv5
ARMv7
(or ARMv8 AArch32 mode)
ARMv8
(AArch64 mode)
32
64
128
32
32
32
16
16
or
or
FP register set1
Advanced SIMD
and FP register set1
SIMD
and FP register set
Evolution of the secondary register set

## Slide 41: 2.2.1 Overview (11b)
FP32/64
Up to 8xFP32 or 4xFP64
operationsc serially executed
Scalar data
Serially processed FP vector data
VFPv1/v2 extension
ARMv5
ARMv7
(or ARMv8 AArch32 mode)
ARMv8
(AArch64 mode)
32
64
64
128
128
32
32
32
16
16
or
or
FP register set1
Advanced SIMD
and FP register set1
SIMD
and FP register set
Secondary register set based FP and SIMD extensions -3

## Slide 42: 2.2.1 Overview (12)
Example: Serially processed 5-element vector operation [65]
In the example the input operands are taken from the registers s10...s14 and
s18...s22, and the result is written into the registers s26...s30.
The execution is sequential (like a hardware implemented subroutine).
A
E.g.
+
B
=
C

## Slide 43: 2.2.1 Overview (11b)
FP32/64
Up to 8xFP32 or 4xFP64
operationsc serially executed
Up to 8xFP32 or 4xFP64
operations serially executed
FP161/32/64
Scalar data
Serially processed FP vector data
VFPv1/v2 extension
ARMv5
ARMv7
(or ARMv8 AArch32 mode)
ARMv8
(AArch64 mode)
32
64
64
128
128
32
32
32
16
16
or
or
FP register set1
Advanced SIMD
and FP register set1
SIMD
and FP register set
VFPv3/v4 extension2
Secondary register set based FP and SIMD extensions -3
Scalar data
Serially processed FP vector data

## Slide 44: 2.2.1 Overview (11b)
FP32/64
Up to 8xFP32 or 4xFP64
operationsc serially executed
Up to 8xFP32 or 4xFP64
operations serially executed
FP161/32/64
Scalar data
Serially processed FP vector data
64/128-bit wide SIMD (vector) data
FX8/16/32/64
FP163/32/64 operations
SIMD data
VFPv1/v2 extension
Advanced SIMD (NEON) extension
ARMv5
ARMv7
(or ARMv8 AArch32 mode)
ARMv8
(AArch64 mode)
32
64
64
128
128
32
32
32
16
16
or
or
FP register set1
Advanced SIMD
and FP register set1
SIMD
and FP register set
VFPv3/v4 extension2
Secondary register set based FP and SIMD extensions -3
Scalar data
Serially processed FP vector data

## Slide 45: 2.2.1 Overview (13)
Example vector data formats of the Advanced SIMD (NEON) extension [86]

## Slide 46: 2.2.1 Overview (11b)
FP32/64
Up to 8xFP32 or 4xFP64
operationsc serially executed
Up to 8xFP32 or 4xFP64
operations serially executed
FP161/32/64
Scalar data
Serially processed FP vector data
64/128-bit wide SIMD (vector) data
FX8/16/32/64
FP163/32/64 operations
SIMD data
VFPv1/v2 extension
Advanced SIMD (NEON) extension
64/128-bit wide SIMD data
FX8/16/32/64
FP163/32/64 operations
FP161/32/64
SIMD and FP extension
ARMv5
ARMv7
(or ARMv8 AArch32 mode)
ARMv8
(AArch64 mode)
32
64
64
128
128
32
32
32
16
16
or
or
FP register set1
Advanced SIMD
and FP register set1
SIMD
and FP register set
VFPv3/v4 extension2
Scalar data
SIMD (vector) data
Secondary register set based FP and SIMD extensions -3
Scalar data
Serially processed FP vector data
1FP16 supports only data conversion
between FP16 and FP32/FP64.

## Slide 47: 2.2.1 Overview (14)
It supports
FX-SIMD operations
It supports
FX/FP scalar and SIMD operations
It supports
FX/FP SIMD operations
on long vector data
The SVE register set based SIMD extension -1
Section 2.2.2
Section 2.2.3
Section 2.2.4
ARMv6
ARMv5
ARMv8.2
SVE: Scalable Vector Extension
The GPR register set based
SIMD extension
A secondary register set added
with FP and SIMD extensions
An SVE register set added
with SIMD extensions
ARM’s ISA extensions to enhance compute capabilities

## Slide 48: 2.2.1 Overview (15)
ARM ISA |  | Name of the extensions | The SVE register set based SIMD extension |  | 
 |  |  | Available register set | Scalar data types | Vector data types
Name | Year |  |  |  | 
ARMv8.2 | 2016 | SVE | SVE register set 32 registers each (1...16)x128-bit wide | --- | FX 8/16/32/64/128 FP 16/32/64 (1...16)x128-bit wide FMA available
The SVE register set based SIMD extension -2
*

## Slide 49: 2.2.1 Overview (16)
Up to 16 x128-bit wide SIMD data
FX8/16/32/64
FP163/32/64 operations
SVE extension
ARMv8.2
(AArch64 mode)
128
32
SVE register set
SIMD (vector) data
---
Up to 16 x 128-bit (Up to 2048-bit)
The SVE register set based SIMD extension -3
*

## Slide 50: 2.2.1 Overview (17)
Data types assuming 256-bit long
SVE registers [116]
8-bit: FX
16-bit: FX/FP
32-bit: FX/FP
64-bit: FX/FP
128-bit: FX
Possible data types

## Slide 51: 2.2.1 Overview (18)
Remarks: See on the slide 2.1 Overview (5).
Overview of the ISA extensions introduced to enhance compute capabilities
ARMv4
ARMv5
ARMv6
ARMv8-A
ARMv7-A/R
Jazelle
(Jazelle DBX)
VFPv1/2
Thumb
(ARMv4T)
SIMD
TrustZone
Thumb-2
(ARMv6T2)
Adv. SIMD1
(NEON)
VFPv3/v42
Crypto-graphy ext.
Jazelle
(ex. by SW)
Jazelle RCT3
(ThumbEE)
ARM710T
(~1995)
ARM926
(2001)
ARM1176
(2004)
Cortex-A5 - A15
(2005)
Cortex-A53/A57
(2012)
Examples
To enhance
security
To speed up
the execution
of bytecodes
To reduce
code size
SVE4
To enhance
compute
capabilities
AArch32
AArch64
Adv. SIMD and FP
SIMD
and FP

## Slide 52
2.2.2 The GPR register set based SIMD extension
Neither this nor all subsequent 2.2.x Sections will be discussed.

## Slide 53: 2.2.2 The GPR register set based SIMD extension (1)
2.2.2 The GPR register set based SIMD extension
Section 2.2.2
Section 2.2.3
Section 2.2.4
It supports
FX-SIMD operations
It supports
FX/FP scalar and SIMD operations
It supports
FX/FP SIMD operations
on long vector data
ARMv6
ARMv5
ARMv8.2
The GPR register set based
SIMD extension
A secondary register set added
with FP and SIMD extensions
An SVE register set added
with SIMD extensions
ARM’s ISA extensions to enhance compute capabilities

## Slide 54: 2.2.2 The GPR register set based SIMD extension (2)
32
31
ARMv3
Previously 26 bitwide)
ARMv8
(Aarch32)
32
13
ARMv7
Evolution of the GPR register set in the ARM ISA -1
GPR register set
64
31
ARMv8
(AArch64)
...
32
13
...

## Slide 55: 2.2.2 The GPR register set based SIMD extension (3)
Stack pointer
Link register
PC
32-bit wide
GPRs in the ARMv3-ARMv7 and the
ARMv8 AArch32 execution mode
GPRs in the ARMv8 AArch64 execution mode
In the AArch64 mode the ARMv8 ISA version expands the number of GPRs
from 13 32-bit registers to 31 64-bit wide registers, as shown in the next Figure.
R0
R1
R2
.
.
.
R12
R13(SP)
R14(LR)
R15(PC)
The GPR register sets in the ARMv3-ARMv7 and the ARM v8 ISA [63], [66]
Dedicated use
Dedicated use
32-bit wide
64-bit wide
32-bit access
64-bit access
X0
X1
X2
.
.
.
X12
X13
X14
.
.
.
X30
X31
X3
W0
W1
W2
.
.
.
W12
W13
W14
.
.
.
W30
W31
W3

## Slide 56: 2.2.2 The GPR register set based SIMD extension (4)
Introduction of the GPR register set based SIMD extension in the ARMv6 ISA
32
31
ARMv3
Previously 26 bitwide)
32
13
ARMv7
GPR register set
64
31
ARMv8
(AArch64)
32
13
...
...
ARMv6
Scalar data
FX32
FX64
SIMD
extension
32-bit wide FX-SIMD FX8/16 operations
Basic ISA
SIMD data
ARMv8
(Aarch32)
32-bit data
64-bit data
32
13
FX32

## Slide 57: 2.2.2 The GPR register set based SIMD extension (4b)
Introduction of the GPR register set based SIMD extension in the ARMv8 ISA
32
31
ARMv3
Previously 26 bitwide)
32
13
ARMv7
GPR register set
64
31
ARMv8
(AArch64)
32
13
...
...
ARMv6
Scalar data
FX32
SIMD
extension
32-bit wide FX-SIMD FX8/16 operations
Basic ISA
SIMD data
32-bit wide FX-SIMD FX8/16 operations
SIMD data
64-bit wide FX-SIMD
FX8/16/32 operations
SIMD data
ARMv8
(Aarch32)
32-bit data
64-bit data
32
13
FX64
FX32

## Slide 58: 2.2.2 The GPR register set based SIMD extension (5)
It supports FX-SIMD operations on 32-bit wide SIMD data in the GPR registers.
Available instructions perform operations on 4xFX8 or 2xFX16 data in parallel.
It is similar to Intel’ s MMX x86 ISA extension from 1997.
The GPR register set based SIMD extension as introduced into the ARMv6 ISA
version provides only a modest performance boosting potential.
By contrast the subsequently, in the ARMv7 ISA version introduced, secondary
register set based advanced SIMD (NEON) extension has a much higher
performance boosting potential.
The GPR register set based SIMD extension

## Slide 59
2. 2.2.3 Secondary register set based FP and SIMD extensions

## Slide 60: 2.2.3.1 Secondary reg. set based FP and SIMD extensions - Overview (1)
2.2.3 Secondary register set based FP and SIMD extensions
2.2.3.1 Secondary register set based FP and SIMD extensions - Overview
Section 2.2.2
Section 2.2.3
Section 2.2.4
It supports
FX-SIMD operations
It supports
FX/FP scalar and SIMD operations
It supports
FX/FP SIMD operations
on long vector data
ARMv6
ARMv5
ARMv8.2
The GPR register set based
SIMD extension
A secondary register set added
with FP and SIMD extensions
An SVE register set added
with SIMD extensions
ARM’s ISA extensions to enhance compute capabilities

## Slide 61: 2.2.3.1 Secondary reg. set based FP and SIMD extensions - Overview (2)
Designation and size of the secondary register set in the ARMv5 - ARMv8 ISAs
ARMv5
ARMv7
(or ARMv8 AArch32 mode)
ARMv8
(AArch64 mode)
32
64
64
128
128
32
32
32
16
16
or
or
FP register set1
Advanced SIMD
and FP register set1
SIMD
and FP register set

## Slide 62: 2.2.3.1 Secondary reg. set based FP and SIMD extensions - Overview (3)
FP32/64
Up to 8xFP32 or 4xFP64
operationsc serially executed
Up to 8xFP32 or 4xFP64
operations serially executed
FP161/32/64
Scalar data
Serially processed FP vector data
64/128-bit wide SIMD (vector) data
FX8/16/32/64
FP163/32/64 operations
SIMD data
VFPv1/v2 extension
Advanced SIMD (NEON) extension
64/128-bit wide SIMD data
FX8/16/32/64
FP163/32/64 operations
FP161/32/64
SIMD and FP extension
ARMv5
ARMv7
(or ARMv8 AArch32 mode)
ARMv8
(AArch64 mode)
32
64
64
128
128
32
32
32
16
16
or
or
FP register set1
Advanced SIMD
and FP register set1
SIMD
and FP register set
VFPv3/v4 extension2
Scalar data
SIMD (vector) data
The secondary register set based FP and SIMD extensions - Overview
Scalar data
Serially processed FP vector data

## Slide 63: 2.2.3.1 Secondary reg. set based FP and SIMD extensions - Overview (4)
1Certain models implement only half of the specified register numbers.
2The implementation of the VFP3 or VFP4 extensions presumes the implemetation of
the Advanced SIMD (NEON) extension.
3In the VFP3/VFP4 extensions only conversions between FP16 and FP32 or FP64 are
supported.
Remarks

## Slide 64: 2.2.3.2 The VFPv1/v2 extensions (1)
2.2.3.2 The VFPv1/v2 extensions
FP32/64
Up to 8xFP32 or 4xFP64
operationsc serially executed
Up to 8xFP32 or 4xFP64
operations serially executed
FP161/32/64
Scalar data
Serially processed FP vector data
64/128-bit wide SIMD (vector) data
FX8/16/32/64
FP163/32/64 operations
SIMD data
VFPv1/v2 extension
Advanced SIMD (NEON) extension
ARMv5
ARMv7
(or ARMv8 AArch32 mode)
ARMv8
(AArch64 mode)
32
64
64
128
128
32
32
32
16
16
or
or
FP register set1
Advanced SIMD
and FP register set1
SIMD
and FP register set
VFPv3/v4 extension2
64/128-bit wide SIMD data
FX8/16/32/64
FP163/32/64 operations
FP161/32/64
SIMD and FP extension
Scalar data
SIMD (vector) data

## Slide 65: 2.2.3.2 The VFPv1/v2 extensions (2)
The FP register set (as introduced in the ARMv5) [65]
Figure: Register banks of the VFP1 and VFP2 extensions [65]
The new secondary register set is 32 x 32-bit or 16x64-bit wide and is
organized as four register banks, each including 8 registers, as seen below.

## Slide 66: 2.2.3.2 The VFPv1/v2 extensions (3)
The first bank is used to hold scalar operands whereas to remaining three banks
vector operands.
FP vector operands may refer to 2 to 8 registers from the same bank.
The vector length is given in a specific field of a control register.
The register numbers given in the instruction specify the first registers that
contain the first operands and specify the first destination register.
Each successive element of the vector is taken by incrementing appropriately the
register numbers.
The peculiarity of the VFP extension is that the elements of the vector are
processed sequentially rather than parallel as for usual SIMD execution.
Use of the FP register set [65]

## Slide 67: 2.2.3.2 The VFPv1/v2 extensions (4)
Example: Serially processed 5-element vector operation [65]
In the example the input operands are taken from the registers s10...s14 and
s18...s22, and the result is written into the registers s26...s30.
The execution is sequential (like a hardware implemented subroutine).

## Slide 68: 2.2.3.3 The VFPv3/v4 extensions (1)
FP32/64
Up to 8xFP32 or 4xFP64
operationsc serially executed
Up to 8xFP32 or 4xFP64
operations serially executed
FP161/32/64
Scalar data
Serially processed FP vector data
64/128-bit wide SIMD (vector) data
FX8/16/32/64
FP163/32/64 operations
SIMD data
VFPv1/v2 extension
Advanced SIMD (NEON) extension
ARMv5
ARMv7
(or ARMv8 AArch32 mode)
ARMv8
(AArch64 mode)
32
64
64
128
128
32
32
32
16
16
or
or
FP register set1
Advanced SIMD
and FP register set1
SIMD
and FP register set
VFPv3/v4 extension2
2.2.3.3 The VFPv3/v4 extensions -1
64/128-bit wide SIMD data
FX8/16/32/64
FP163/32/64 operations
FP161/32/64
SIMD and FP extension
Scalar data
SIMD (vector) data

## Slide 69: 2.2.3.3 The VFPv3/v4 extensions (2)
The VFPv3 and VFPv4 extensions -2
The underlying register set (called the Advanced SIMD and FP register set) is
an extension of the previous FP register set and is shared by the NEON
(Advanced SIMD and FP) extension.
ARMv5
ARMv7
(or ARMv8 AArch32 mode)
32
64
64
128
32
32
16
16
or
or
FP register set1
Advanced SIMD
and FP register set1
Figure: Extension of the secondary register set in the ARMv7 ISA

## Slide 70: 2.2.3.3 The VFPv3/v4 extensions (3)
The VFPv3 and VFPv4 extensions -3
The VFPv3/v4 extensions support basically the same operations as the previous
VFPv2 extension.
The main enhancements of VFPv3/v4 are:
VFPv3 support in addition FP16 (half-word FP) operations, nevertheless
the supported operations are restricted only to conversions between
FP16 and FP32 or FP64 data types.
VFPv4's main enhancement is support of FMA (Fused Multiply Add)
operations.

## Slide 71: 2.2.3.3 The VFPv3/v4 extensions (4)
Contrasting main features of the VFPv1/v2 and VFPv3/v4 extensions
VFP (Vector Floating Point) extensions
VFPv1/v2
VFPv3/v4
Introduced in the ISA version
ARMv5
Introduced in the ISA version
ARMv6
doubling the size of the FP register set to
32x64 or 16x128 bit registers, and
supporting oprations as in case of the previous
vFPv2 version plus
introduction of an FP register set
(32x32 or 16x64 bit)
supporting operations on
scalar FP data (FP32/FP64) and
serially processed FP vector data
(up to 8xFP32 or 4xFP64)
providing instructions that perform
conversions between FP16 and FP32
or FP64 data (since the VFP3) and
additonally FMA operations (in the
VFP4 extension).

## Slide 72: 2.2.3.4 Advanced SIMD (NEON) extension (1)
FP32/64
Up to 8xFP32 or 4xFP64
operationsc serially executed
Up to 8xFP32 or 4xFP64
operations serially executed
FP161/32/64
Scalar data
Serially processed FP vector data
64/128-bit wide SIMD (vector) data
FX8/16/32/64
FP163/32/64 operations
SIMD data
VFPv1/v2 extension
Advanced SIMD (NEON) extension
ARMv5
ARMv7
(or ARMv8 AArch32 mode)
ARMv8
(AArch64 mode)
32
64
64
128
128
32
32
32
16
16
or
or
FP register set1
Advanced SIMD
and FP register set1
SIMD
and FP register set
VFPv3/v4 extension2
2.2.3.4 Advanced SIMD (NEON) extension -1
64/128-bit wide SIMD data
FX8/16/32/64
FP163/32/64 operations
FP161/32/64
SIMD and FP extension
Scalar data
SIMD (vector) data

## Slide 73: 2.2.3.4 Advanced SIMD (NEON) extension (2)
2.2.3.4 The Advanced SIMD (NEON) extension of the ARMv7 -1
NEON shares its register set with the VFPv3/v4 extension.
The shared register set is called the Advanced SIMD and FP register set.
It is an extension of the previous FP register set, as shown in the Figure below.
ARMv5
ARMv7
(or ARMv8 AArch32 mode)
32
64
64
128
32
32
16
16
or
or
FP register set1
Advanced SIMD
and FP register set1
Figure: Extension of the secondary register set in the ARMv7 ISA

## Slide 74: 2.2.3.4 Advanced SIMD (NEON) extension (3)
NEON is intended to accelerate multimedia and signal processing algorithms
such as video encode/decode, 2D/3D graphics, gaming, speech or image
processing.
2.2.3.4 The Advanced SIMD (NEON) extension of the ARMv7 [11] -2

## Slide 75: 2.2.3.4 Advanced SIMD (NEON) extension (4)
NEON instructions operate on 64 or 128-bit wide vectors with
The Advanced SIMD (NEON) extension of the ARMv7 ISA [11] -2
Figure: SIMD data [11]
NEON instructions operate on 64 or 128-bit wide vector data (SIMD data) held
in the Advanced SIMD and FP register set.
FX8/FX16/FX32/FX64 or
FP16/FP32/FP64
For FP16 data NEON supports only conversions between FP16 and FP32/FP64 data.
FP16 data operations are supported only in the Advanced SIMDv2 option.
data elements.
Remark
They perform the same operation on all data elements, as indicated below.

## Slide 76: 2.2.3.4 Advanced SIMD (NEON) extension (5)
Example vector data formats of the Advanced SIMD (NEON) extension [86]

## Slide 77: 2.2.3.5 The SIMD and FP extension of the ARMv8 ISA in AArch64 mode (1)
FP32/64
Up to 8xFP32 or 4xFP64
operationsc serially executed
Up to 8xFP32 or 4xFP64
operations serially executed
FP161/32/64
Scalar data
Serially processed FP vector data
64/128-bit wide SIMD (vector) data
FX8/16/32/64
FP163/32/64 operations
SIMD data
VFPv1/v2 extension
Advanced SIMD (NEON) extension
ARMv5
ARMv7
(or ARMv8 AArch32 mode)
ARMv8
(AArch64 mode)
32
64
64
128
128
32
32
32
16
16
or
or
FP register set1
Advanced SIMD
and FP register set1
SIMD
and FP register set
VFPv3/v4 extension2
2.2.3.5 The SIMD and FP extension of the ARMv8 ISA in the AArch64 mode-1
64/128-bit wide SIMD data
FX8/16/32/64
FP163/32/64 operations
FP161/32/64
SIMD and FP extension
Scalar data
SIMD (vector) data

## Slide 78: 2.2.3.5 The SIMD and FP extension of the ARMv8 ISA in AArch64 mode (2)
The SIMD and FP extension of the ARMv8 ISA in the AArch64 mode -2
Execution modes of the ARMv8
Aarch32
execution mode
It supports two 32-bit instruction sets,
the A32 and the T32 (Thumb) instructions sets.
In this mode the processor can run programs
developed for previous ISA versions.
The ARMv8 ISA version introduces major changes in the ARM architecture while
maintaining a high level of consistency with previous versions of the architecture.
Aarch64
execution mode
It supports a single 64-bit instruction set,
called A64.
This is a fixed length powerful instruction set
that uses 32-bit instruction encodings.
ARMv8 has two distinct execution modes, as indicated below.

## Slide 79: 2.2.3.5 The SIMD and FP extension of the ARMv8 ISA in AArch64 mode (3)
128-bit wide
128-bit wide
V0
V1
V2
.
.
.
V13
V14
V15
V0
V1
V2
.
.
.
V13
V14
.
.
.
V30
V31
V15
64-bit wide
V0
V1
V2
.
.
.
V13
V14
.
.
.
V30
V31
V15
Extension of the secondary register set in the ARMv8 ISA [66]
The AArch64 mode the ARMv8 ISA expands the number of the secondary registers
from 32x64-bit or 16x64-bit (ARMv7 ISA) to 32x128-bit, as seen below.
or
FP and advanced SIMD registers in the ARMv7 and ARMv8 AArch32 execution mode of the ARM ISA
SIMD and FP registers
in the ARMv8 AArch64 execution mode of the ARM ISA

## Slide 80: 2.2.3.5 The SIMD and FP extension of the ARMv8 ISA in AArch64 mode (4)
Use cases of 64- and 128-bit wide SIMD data in the AArch64 mode [66]

## Slide 81
2. 2.2.4 The SVE register set based SVE extension

## Slide 82: 2.2.4 The SVE register set based SVE extension (1)
2.2.4 The SVE register set based SVE extension
Section 2.2.2
Section 2.2.3
Section 2.2.4
It supports
FX-SIMD operations
It supports
FX/FP scalar and SIMD operations
It supports
FX/FP SIMD operations
on long vector data
ARMv6
ARMv5
ARMv8.2
The GPR register set based
SIMD extension
A secondary register set added
with FP and SIMD extensions
An SVE register set added
with SIMD extensions
ARM’s ISA extensions to enhance compute capabilities

## Slide 83: 2.2.4 The SVE register set based SVE extension (2)
The SVE (Scalable Vector Extension) introduced into the AArch64 mode
of the ARMv8 ISA [96]
It was announced in 8/2016 (in the Hot Chips conference).
General specification became available as the ARM Architecture Reference
Manual Supplement - The Scalable Vector Extension (SVE) for ARMv8-A
(β version in 3/2017).
The vector length in SPE is a hardware choice from 1x128 bit to 16x128 bit,
first implementions (e.g. by Fujitsu) choose 4x128 bit = 512 bit vector length.
SVE is implemented only in the AArch64 version of ARMv8.
SVE aims at HPC scientific workloads rather than media or image processing.
It supports both FX and FP processing.

## Slide 84: 2.2.4 The SVE register set based SVE extension (3)
ARMv8
(AArch64 mode)
128
32
The SVE register set introduced in the AArch64 mode of the ARMv8 ISA
128
. . .
(1...16)x128
SVE register set

## Slide 85: 2.2.4 The SVE register set based SVE extension (4)
Avalable SVE registers [96]
LEN: 1 to 16

## Slide 86: 2.2.4 The SVE register set based SVE extension (5)
ARMv8
(AArch64 mode)
128
32
The SVE extension - Overview
(1...16)x 128 bit wide SIMD data
(Supported operations not yet specified)
FX and FP datatypes
(Specified in the ARM Architecture
Reference Manual Supplement -
The Scalable Vector Extension (SVE)
for ARMv8-A)
SVE extension
128
. . .
(1...16)x128
SVE register set

## Slide 87: 2.2.4 The SVE register set based SVE extension (6)
The SVE instruction set [96]

## Slide 88: 2.2.4 The SVE register set based SVE extension (7)
Example: Use of 256-bit vectors (either for FX or FP computations) [96]

## Slide 89: 2.2.4 The SVE register set based SVE extension (8)
Speed-up potential of SVE [96]

## Slide 90
2.3 ISA extensions introduced to reduce code size
(Not discussed)

## Slide 91: 2.3.1 ISA extensions introduced to reduce code size - Overview (1)
ISA extensions
to enhance
compute capabilities
ARM’s ISA extensions
ISA extensions
to speed up
the execution of bytecodes
ISA extensions
to enhance
security
ISA extensions
to reduce
code size
Section 2.2
Section 2.3
Section 2.4
Section 2.5
2.3 ISA extensions introduced to reduce code size
2.3.1 ISA extensions introduced to reduce code size - Overview (1)

## Slide 92: 2.3.1 ISA extensions introduced to reduce code size - Overview (2)
ARMv4
ARMv5
ARMv6
ARMv8-A
ARMv7-A/R
Jazelle
(Jazelle DBX)
VFPv1/2
Thumb
(ARMv4T)
SIMD
TrustZone
Thumb-2
(ARMv6T2)
Adv. SIMD1
(NEON)
VFPv3/v42
Crypto-graphy ext.
Jazelle
(ex. by SW)
Jazelle RCT3
(ThumbEE)
ARM710T
(~1995)
ARM926
(2001)
ARM1176
(2004)
Cortex-A5 - A15
(2005)
Cortex-A53/A57
(2012)
Examples
To enhance
security
To speed up
the execution
of bytecodes
SVE4
To enhance
compute
capabilities
AArch32
AArch64
Remarks: See on the slide 2.1 Overview (5)
ISA extensions introduced to reduce code size - Overview (2) (Based on [64])
To reduce
code size
Adv. SIMD and FP
SIMD
and FP

## Slide 93: 2.3.1 ISA extensions introduced to reduce code size - Overview (3)
ISA extensions to reduce code size
The Thumb instruction set
(ARMv4/~1995))
The Thumb-2 instruction set
(ARMv6/~2005))
Only 16-bit Thumb instructions
Both 16 and 32-bit Thumb instructions
ISA extensions introduced to reduce code size - Overview (3)
(Section 2.3.2)
(Section 2.3.3)

## Slide 94: 2.3.2 The Thumb instruction set (1)
2.3.2 The Thumb instruction set [67]
This is an alternative 16-bit instruction set that provides typically 35 to 40 %
better code density than traditional ARM code but reduces performance slightly,
e.g. by 10 %.
It has been introduced in the ARMv4 ISA.
Processors with the T suffix provide beyond the default 32-bit ARM also the
16-bit Thumb instruction set.
Thumb instructions are 16-bit long, most 32-bit ARM instructions can be recoded
to a single 16-bit Thumb instruction format.
The Thumb instruction set is a subset of the ARM instruction set.
There is a special instruction for entering the Thumb state (BX).
Compilers are usually able to generate code optinally either for the ARM or the
Thumb ISA.
In the Thumb instructon set there are only 8 GPRs available for the programmer,
as shown in the next Figure.

## Slide 95: 2.3.2 The Thumb instruction set (2)
Available GPR register sets in the ARM and the Thumb ISA [63]

## Slide 96: 2.3.3 The Thumb-2 instruction set (1)
2.3.3 The Thumb-2 instruction set [79]
It was introduced along with the ARM1156T2-S processor in 2005.
Thumb-2 is a superset of the 16-bit ARMv6 Thumb iSA.
It adds several new 16-bit instructions and also 32-bit instructions that can be
freely intermixed in a program.
The enhancements allow Thumb-2 to more efficiently cover the functionality of
the ARM instruction set.
In subsequent processors Thumb-2 replaced the Thumb instruction set.

## Slide 97
2.4 ISA extensions to speed up
the execution of bytecodes
(Not discussed)

## Slide 98: 2.4.1 ISA extensions to speed up the execution of bytecodes - Overview (1)
ISA extensions
to enhance
compute capabilities
ARM’s ISA extensions
ISA extensions
to speed up
the execution of bytecodes
ISA extensions
to enhance
security
ISA extensions
to reduce
code size
Section 2.2
Section 2.3
Section 2.4
Section 2.5
2.4 ISA extensions introduced to speed up the execution of bytecodes
2.4.1 ISA extensions introduced to speed up the execution of bytecodes
- Overview (1)

## Slide 99: 2.4.1 ISA extensions to speed up the execution of bytecodes - Overview (2)
ARMv4
ARMv5
ARMv6
ARMv8-A
ARMv7-A/R
Jazelle
(Jazelle DBX)
VFPv1/2
Thumb
(ARMv4T)
SIMD
TrustZone
Thumb-2
(ARMv6T2)
Adv. SIMD1
(NEON)
VFPv3/v42
Crypto-graphy ext.
Jazelle
(ex. by SW)
Jazelle RCT3
(ThumbEE)
ARM710T
(~1995)
ARM926
(2001)
ARM1176
(2004)
Cortex-A5 - A15
(2005)
Cortex-A53/A57
(2012)
Examples
To enhance
security
To reduce
code size
SVE4
To enhance
compute
capabilities
AArch32
AArch64
Remarks: See on the slide 2.1 Overview (5).
ISA extensions introduced to speed up the execution of bytecodes
Overview (2) (Based on [64])
To speed up
the execution
of bytecodes
Adv. SIMD and FP
SIMD
and FP

## Slide 100: 2.4.1 ISA extensions to speed up the execution of bytecodes - Overview (3)
ISA extensions to speed up the execution of bytecodes - Overview (3)
Jazelle RCT (ThumbEE)
Trivial implementation of Jazelle1
Jazelle RCT (ThumbEE)
Depricated,
no more support
in ARMv8 processors
Speeds up bytecode execution
with JIT or AOT compilation.
Possible use for Java, .NET MSIL,
Python, Perl etc.
ARMv7-A
Issue A
Cortex-A8
(2005)
ARMv7-A
Issue C
Cortex-A57/A53
(2012)
ARMv8
(2011)
Implemented for compatibility.
Does not accelerate the execution
of bytecodes,
the JVM uses software routines
to execute them.
Section 2.4.3
Section 2.4.4
+
1A few ARMv7 processors, such as the Cortex-A5 and the Cortex-A9 support Jazelle DBX as an option.
Jazelle
(Jazelle DBX)
Speeds up the execution
of Java bytecode
on resource-constrained
devices by partially
hardware support.
ARMv5TEJ
ARM926
(2001)
E.g.
Section 2.4.2

## Slide 101: 2.4.2 Jazelle (Jazelle DBX) (1)
Jazelle RCT (ThumbEE)
Trivial implementation of Jazelle1
Jazelle RCT (ThumbEE)
Depricated,
no more support
in ARMv8 processors
Speeds up bytecode execution
with JIT or AOT compilation.
Possible use for Java, .NET MSIL,
Python, Perl etc.
ARMv7-A
Issue A
Cortex-A8
(2005)
ARMv7-A
Issue C
Cortex-A57/A53
(2012)
ARMv8
(2011)
Does not accelerate the execution
of bytecodes,
the JVM uses software routines
to execute them.
Section 2.4.3
Section 2.4.4
+
1A few ARMv7 processors, such as the Cortex-A5 and the Cortex-A9 support Jazelle DBX as an option.
2.4.2 Jazelle (Jazelle DBX) -1
Jazelle
(Jazelle DBX)
Speeds up the execution
of Java bytecode
on resource-constrained
devices by partially
hardware support.
ARMv5TEJ
ARM926
(2001)
E.g.
Section 2.4.2

## Slide 102: 2.4.2 Jazelle (Jazelle DBX) (2)
2.4.2 Jazelle (Jazelle DBX) -2
It is ARM’s third ISA option, introduced in the ARMv5TEJ ISA (in 2001), as indicated
below.
Figure: The Jazelle ISA extension as ARM’s third ISA alternative [67]
It aims at accelerating the execution of Java bytecode.

## Slide 103: 2.4.2 Jazelle (Jazelle DBX) (3)
Java bytecode
It is one kind of bytecodes.
Bytecodes are compact 1-byte codes written for a stack based virtual machine
(virtual ISA).
All opcodes are one byte long followed by optional parameters.

## Slide 104: 2.4.2 Jazelle (Jazelle DBX) (4)
Part of a Java
bytecode [80]

## Slide 105: 2.4.2 Jazelle (Jazelle DBX) (5)
The computational model assumed for bytecodes
The computational model of bytecodes presumes a stack based execution, i.e.
operands are first loaded into the stack and operations will be executed on the
operands being in the stack.

## Slide 106: 2.4.2 Jazelle (Jazelle DBX) (6)
Bytecodes are generated by compiling a source code assuming a virtual ISA
that is underlying the considered bytecode and is not bound to any real ISA,
like the ARM or x86 ISA.
So bytecodes can not be directly run on any processor, i.e. they are a kind of
pseudocode that can be executed by a virtual machine, as indicated in the
next Figure for the Java bytecode.
Principle of generating and executing Java bytecode -1 [81]

## Slide 107: 2.4.2 Jazelle (Jazelle DBX) (7)
Principle of generating and executing Java bytecode -2 [81]

## Slide 108: 2.4.2 Jazelle (Jazelle DBX) (8)
Generating and executing Java bytecode on different platforms [82]
It is the task of the Java compiler to generate the Java bytecode from a given
source language.
The Java compiler runs under a given OS on a particular platform, as seen
in the Figure below.
Figure: Principle of generating Java bytecode [82]

## Slide 109: 2.4.2 Jazelle (Jazelle DBX) (9)
The most straightforward way to implement a Java Virtual Machine or virtual
machines at all is to use a software interpreter as a virtual machine.
A faster implementation can be achieved by compiling the bytecode by a JIT or
AOT compiler (as seen in the next Figure and discussed in Section 3.3.3)
on the processor itself and/or by using hardware support for the execution,
such as ARM's Jazelle DBX or a coprocessor.
Principle of executing Java bytecode [83]

## Slide 110: 2.4.2 Jazelle (Jazelle DBX) (10)
Implementing a Java Virtual Machine by including a JIT compiler into it [83]

## Slide 111: 2.4.2 Jazelle (Jazelle DBX) (11)
Portability of the Java bytecode or bytecodes at all
Since bytecodes are not bound to a particular real ISA but will be executed
by a virtual machine that suits the target ISA and target OS, bytecodes are
portable.
It follows that for a given type of bytecode, e.g. Java bytecode, there are many
possible virtual machines, as the next Figure indicates.

## Slide 112: 2.4.2 Jazelle (Jazelle DBX) (12)
The bytecode is processed by the JVM
component of the Java Runtime
Environment (JRE).
Each platform needs one or more JVMs
that suits the OS and the target ISA,
as indicated in the Figure.
It is then the task of the JVM to execute
the bytecode e.g. by interpreting each
bytecode instructions.
Example: Executing Java bytecode on different platforms
Figure: Different JVMs for different OSs and CPU ISA [84]

## Slide 113: 2.4.2 Jazelle (Jazelle DBX) (13)
Jazelle DBX support for executing Java bytecode on ARM processors
An inherent drawback of interpreting Java bytecode vs. compiled execution is
slower speed.
Jazelle DBX aims at mitigating this drawback by providing hardware support
for executing Java bytecode.
For this reason Jazelle DBX provides a third execution state, called the Jaselle
processor state, where the processor decodes Java bytecode to ARM
instructions as follows:
about 2/3 of Java bytecode will directly be mapped to ARM instructions, and
the remainder will be trapped as exceptions and emulated by multiple ARM
instructions via rougly 8 kB of microcode memory.
A special instruction (the BXJ instruction) is used to switch the processor from
the ARM state to the Jazelle state.
Jazelle DBX was introduced in the ARMv5 based ARM926 in 2001 and was used
in ARMv5 and ARMv6 processor implementations typically with very limited
memory.

## Slide 114: 2.4.2 Jazelle (Jazelle DBX) (14)
Implementation of Jazelle DBX [67]

## Slide 115: 2.4.2 Jazelle (Jazelle DBX) (15)
JDK (Java Developer Kit) contains
tools needed for developing Java
programs, such as the compiler
(javac.exe), etc.
The compiler converts Java code
into byte code.
JRE (Java Runtime Environment)
contains JVM that actually runs
the Java program, class libraries
and other supporting files.
JVM (Java Virtual Machine) runs
the program, and it uses the
class libraries, and other
supporting files provided in JRE.
To run Java programs, the fitting
JRE needs to be installed on the
system.
JVM itself is not platform independent.
When JVM has to interpret the byte codes to machine language, then it has to
interact with the OS and interpretes Java bytecode on the ARM ISA.
Figure: The Java programming environment [85]
Remark 1: The Java programming environment [85]

## Slide 116: 2.4.2 Jazelle (Jazelle DBX) (16)
.Net native deep dive
Remark 2: Code generation in .NET
Figure: Code generation in .NET [88]
A further example for making use of the virtual machine principle is Microsoft's
MSIL bytecode (officially known as CIL (Common Intermediate language)), that is
utilized by the .NET framwork (see the Figure below).

## Slide 117: 2.4.3 Jazelle RCT (Runtime Compilation Target) (1)
Jazelle RCT (ThumbEE)
Trivial implementation of Jazelle1
Jazelle RCT (ThumbEE)
Depricated,
no more support
in ARMv8 processors
Speeds up bytecode execution
with JIT or AOT compilation.
Possible use for Java, .NET MSIL,
Python, Perl etc.
ARMv7-A
Issue A
Cortex-A8
(2005)
ARMv7-A
Issue C
Cortex-A57/A53
(2012)
ARMv8
(2011)
Does not accelerate the execution
of bytecodes,
the JVM uses software routines
to execute them.
Section 2.4.3
Section 2.4.4
+
1A few ARMv7 processors, such as the Cortex-A5 and the Cortex-A9 support Jazelle DBX as an option.
2.4.3 Jazelle RCT (Runtime Compilation Target) -1
It was introduced in 2005 (along with the first Cortex processor (Cortex-A8),
based on the ARMv7 Issue A,) but withdrawn in 2011 (with the ARMv7 Issue C,)
as seen below.
Jazelle
(Jazelle DBX)
Speeds up the execution
of Java bytecode
on resource-constrained
devices by partially
hardware support.
ARMv5TEJ
ARM926
(2001)
E.g.
Section 2.4.2

## Slide 118: 2.4.3 Jazelle RCT (Runtime Compilation Target) (2)
Jazelle RCT (Runtime Compilation Target) [86] -2
Jazelle RCT is dubbed also as the ThumbEE extension, since it makes use
of the ThumEE execution environment that is based on an enhanced version
of the Thumb2 instruction set.
It aims at speeding up the execution of dynamically generated code.
This is code that is compiled e.g. from a portable bytecode e.g. Java, Perl, Python
bytecode or .Net MSIL, on the processor
either while downloading the bytecode (by an Ahead-Of-Time or AOT
compiler) or
during execution of the code (by an Just-In-Time compiler).

## Slide 119: 2.4.3 Jazelle RCT (Runtime Compilation Target) (3)
Example: Just-in-time (JIT) compilation in Java environment [73]
Java bytecode is loaded, compiled to native code each time a method is called, compiled code is cached in memory and will be executed by the Java Virtual Machine (JVM), as shwn below.
Figure: Just-in-time compilation in Java einvironment [73]
Platform neutral
portable bytecode
Extensions
JVM
ThumbEE ISA support

## Slide 120: 2.4.3 Jazelle RCT (Runtime Compilation Target) (4)
Benefits of using Jaselle RCT [67]
It provides a higher speed up in executing bytecode than Jaselle DBX but requires
more memory.
It follows that the introduction of Jazelle RCT (ThumbEE) made Jazelle DBX
more or less superfluous.
As a consequence, when ARMv7 based Cortex-A processors introduced
Jazelle RCT(ThumbEE), at the same time they typically stopped supporting
Jazelle DBX.
(In fact, the Cortex-A8/A7 or A15 processors as well as the subsequent ARMv8
based processors provided instead only a trivial (software emulated) Jazelle
implementation (see Section 2.4.4) whereas the Cortex-A5 and A9 processos
supported Jazelle DBX as an option).

## Slide 121: 2.4.3 Jazelle RCT (Runtime Compilation Target) (5)
Drawbacks of dynamic compilation [67]
AOT or JIT compilation causes a delay between an application's launch and its
actual run, this can prevent their use in real time application.
Further on, dynamically compiled code expands four to six times.
So, in addition to delaying the startup of an application, AOT and JIT compilation
requires extra memory for the code compiled.
As a consequence, ARM depricated the use of the Jazelle RCT (ThumbEE)
ISA extension in the ARMv7 Issue C (10/2011) and subsequent ARMv8 ISA.

## Slide 122: 2.4.4 Trivial implementation of Jazelle (1)
Jazelle RCT (ThumbEE)
Trivial implementation of Jazelle1
Jazelle RCT (ThumbEE)
Depricated,
no more support
in ARMv8 processors
Speeds up bytecode execution
with JIT or AOT compilation.
Possible use for Java, .NET MSIL,
Python, Perl etc.
ARMv7-A
Issue A
Cortex-A8
(2005)
ARMv7-A
Issue C
Cortex-A57/A53
(2012)
ARMv8
(2011)
Does not accelerate the execution
of bytecodes,
the JVM uses software routines
to execute them.
Section 2.4.3
Section 2.4.4
+
1A few ARMv7 processors, such as the Cortex-A5 and the Cortex-A9 support Jazelle DBX as an option.
2.4.4 Trivial implementation of Jazelle -1
Jazelle
(Jazelle DBX)
Speeds up the execution
of Java bytecode
on resource-constrained
devices by partially
hardware support.
ARMv5TEJ
ARM926
(2001)
E.g.
Section 2.4.2

## Slide 123: 2.4.4 Trivial implementation of Jazelle (2)
Trivial implementation of Jazelle -2 [87]
In the trivial Jazelle implementation, the processor does not accelerate
the execution of any bytecodes, JVM uses software routines to execute any
bytecode.
The introduction of Jazelle RCT in Cortex-A processors made Jazelle DBX obsolete,
but for reasons of compatibility, in subsequent processors ARM provided a
so called trivial implementation of Jazelle.

## Slide 124
2.5 ISA extensions introduced to enhance security
(Not discussed)

## Slide 125: 2.5.1 ISA extensions introduced to enhance security - Overview (1)
ISA extensions
to enhance
compute capabilities
ARM’s ISA extensions
ISA extensions
to speed up
the execution of bytecodes
ISA extensions
to enhance
security
ISA extensions
to reduce
code size
Section 2.2
Section 2.3
Section 2.4
Section 2.5
2.5 ISA extensions introduced to enhance security
2.5.1 ISA extensions introduced to enhance security - Overview (1)

## Slide 126: 2.5.1 ISA extensions introduced to enhance security - Overview (2)
ARMv4
ARMv5
ARMv6
ARMv8.0-A
ARMv7-A/R
Jazelle
(Jazelle DBX)
VFPv1/2
Thumb
(ARMv4T)
SIMD
TrustZone
Thumb-2
(ARMv6T2)
Adv. SIMD1
(NEON)
VFPv3/v42
Crypto-graphy ext.
Jazelle
(ex. by SW)
Jazelle RCT3
(ThumbEE)
ARM710T
(~1995)
ARM926
(2001)
ARM1176
(2004)
Cortex-A5 - A15
(2005)
Cortex-A53/A57
(2012)
Examples
To reduce
code size
SVE4
To enhance
compute
capabilities
AArch32
AArch64
Remarks: See on the slide 2.1 Overview (5).
To speed up
the execution
of bytecodes
To enhance
security
ISA extensions introduced to enhance security - Overview (2)
(Based on [64])
Adv. SIMD and FP
SIMD
and FP

## Slide 127: 2.5.1 ISA extensions introduced to enhance security - Overview (3)
The TrustZone extension
ISA extensios nroduced to enhance security
The Cryptography extension
ARMv6 (2001)
ARMv8 (2012)
Section 2.5.2
Section 2.5.3
ISA extensions introduced to enhance security - Overview (3)

## Slide 128: 2.5.2 The TrustZone extension (1)
2.5.2 The TrustZone extension [68]
It is achieved by partitioning system wide hardware and software resources so
that they exist in one of two worlds;
in the Secure world for the security subsystem and
the Normal world for everything else.
Hardware logic of the TrustZone ensures that no Secure world resources can be
accessed from the Normal world.
For details see e.g. [68].
It provides a system-wide protection against possible attacks.
The trustZone extension was introduced as part of the ARMv6 ISA.

## Slide 129: 2.5.3 The Cryptography extension (1)
2.5.3 The Cryptography extension [69]
It adds new instructions to accelerate the execution of cryptographic algorithms,
like
Encryption/decryption according to the Advanced Encryption Standard (AES),
Secure Hash Algorithm (SHA) functions SHA-1, SHA-224, and SHA-256.
It is similar to Intel’s AES-NI ISA extension introduced along with the Westmere
basic architecture (2009).
It was introduced as part of the ARMv8 ISA.

## Slide 130
3. Overview of ARM’s processor series
3.1 Overview
3.2 Processors implementing the ARMv1 – ARMv2 ISA
3.3 Processors implementing the ARMv3 – ARMv6 ISA
3.4 Processors implementing the ARMv7 – ARMv8 ISA
Only Section 3.4 will be discussed.

## Slide 131
3.1 Overview of ARM’s processor series

## Slide 132: 3.1 Overview of ARM’s processor series (1)
3.1 Overview
Subsequently, we give an overview of ARM’s processor series subdivided into three
sections, according their underlying ISAs, as follows.
Processors implementing
the ARMv1 – ARMv2 ISA
ARM’s processor series
(Earliest ARM processors)
(~ 1985-1990)
ARM1-ARM3
26-bit address bus
32-bit data buses
Processors implementing the ARMv3 – v6 ISA
(Early ARM processors)
(~ 1991-2004)
ARM6xx-ARM11xx
32-bit address bus
32-bit data buses
Processors implementing
the ARMv7 – ARMv8 ISA
(ARM’s Cortex processors)
(Since 2004/2012)
Cortex lines
ARMv7: 32-bit
ARMv8: 64-bit
with AArch64 and AArch32 modes
(Section 3.2)
(Section 3.3)
(Section 3.4)

## Slide 133
3.2 Processors implementing the ARM v1 - ARM v2 ISA

## Slide 134: 3.2 Processors implementing the ARM v1 - ARM v2 ISA (1)
3.2 Processors implementing the ARMv1 – ARMv2 ISA -1 [5]

## Slide 135: 3.2 Processors implementing the ARM v1 - ARM v2 ISA (2)
Remarks
processors based on the ARM ISA versions ARMv1 and ARMv2 (like ARM1,
ARM2 or ARM3) implement only a 26-bit address bus and a 32-bit data bus.
They are called 26-bit architectures.
By contrast, processors based on the ARMv3 or higher ISA version support
already a 32-bit address space and are known as 32-bit architectures
up to the ARMv7 ISA.
In the ARMv8 ISA the AArch64 mode supports already 64-bit addressing.
As already discussed in Section 2.1

## Slide 136
3.3 Processors implementing the ARM v3 - ARM v6 ISA

## Slide 137: 3.3 Processors implementing the ARM v3 - ARM v6 ISA (1)
3.3 Processors implementing the ARMv3 – ARMv6 ISA [5]

## Slide 138: 3.3 Processors implementing the ARM v3 - ARM v6 ISA (2)
ARMv4
ARMv5
ARMv6
ARMv8-A
ARMv7-A/R
Jazelle
(Jazelle DBX)
VFPv1/2
Thumb
(ARMv4T)
SIMD
TrustZone
Thumb-2
(ARMv6T2)
Adv. SIMD1
(NEON)
VFPv3/v42
Crypto-graphy ext.
Jazelle
(ex. by SW)
Jazelle RCT3
(ThumbEE)
ARM710T
(~1995)
ARM926
(2001)
ARM1176
(2004)
Cortex-A5 - A15
(2005)
Cortex-A53/A57
(2012)
Examples
To reduce
code size
SVE4
To enhance
compute
capabilities
AArch32
AArch64
Remarks: See on the slide 2.1 Overview (5).
To speed up
the execution
of bytecodes
To enhance
security
Main extensions introduced in the ARMv4 – ARM v6 ISA versions (simplified)

## Slide 139: 3.3 Processors implementing the ARM v3 - ARM v6 ISA (3)
XScale is a trademark of Intel Corporation
Overview of ARM’s processors implementing the ARMv4 – ARMv6 ISA [5]
1998
2000
2002
2004
time
version
ARMv5
ARMv6
1994
1996
2006
ARMV4
StrongARM
ARM926EJ-S
XScale
ARM102xE
ARM1026EJ-S
ARM9x6E
ARM92xT
ARM1136JF-S™
ARM7TDMI-S
ARM720T
SC100
SC200
ARM1176JZF-S
ARM1156T2F-S
ARM1136JF-S™
Notes: Versions mostly refer to the instruction set that the ARM core executes.
The ARM7, which is still the most often used core in a low-power design, executes the version 4T instruction set. Architectural extensions were added for version 5TE to include DSP instructions, such as 16-bit signed MLA instructions, saturation arithmetic, etc. The ARM926EJ-S and ARM1026EJ-S cores are examples of Version 5 architectures. Version 6 added instructions for doing byte manipulations and graphics algorithms more efficiently. The ARM11 family implemented the Version 6 architecture. Version 7 architectures (which include the Cortex family of cores, such as the Cortex A8, Cortex M3 and Cortex R4) extended the functionality by adding things such as Thumb2, low-power features, and more security.

## Slide 140: 3.3 Processors implementing the ARM v3 - ARM v6 ISA (4)
Evolution of the pipeline length of ARM v4 – ARM v6 based processors [8]
ARMv4
ARMv4
ARMv5
ARMv5
ARMv6

## Slide 141: 3.3 Processors implementing the ARM v3 - ARM v6 ISA (5)
Main features of the ARMv5 – ARMv6 processors (≈1999-2003) [57]

## Slide 142: 3.3 Processors implementing the ARM v3 - ARM v6 ISA (6)
Introduction of multicore processors by ARM: the ARM11 MPCore
07/2003: First public disclosure of the ARM11 MPCore.
05/2004: ARM11 MPCore (multi core ARM11 with 1-4 cores) available for licensing
with an evaluation system for early software development.
IEM (Intelligent Energy Manager)
It dynamically predicts the required performance and lowers the voltage and
the frequency accordingly.
The ARM11 MPCore incorporates:
It is basically an up to four way (4-socket) cache coherent symmetric multicore
processor

## Slide 143: 3.3 Processors implementing the ARM v3 - ARM v6 ISA (7)
Block diagram of the ARM11 MPCore [9]
Note that the ARM11 MPCore does not include an L2.

## Slide 144: 3.3 Processors implementing the ARM v3 - ARM v6 ISA (8)
Year of launching | Dual core design
10/2001 | IBM launches dual core POWER4
11/2002 | IBM launches dual core POWER4+
03/2004 | Sun releases the UltraSPARC IV (Jaguar) dual core processor
05/2004 | ARM announces the availability of the synthetizable ARM11 MPCore quad core processor
05/2004 | IBM launches dual core POWER5
08/2004 | AMD demonstrates first x86 dual core (Opteron) processor
04/2005 | ARM demonstrates the ARM11 MPCore quad core test chip in cooperation with NEC
04/2005 | Intel launches dual core Pentium processors (Pentium D)
04/2005 | AMD launches dual core Opteron server processors
06/2006 | Intel launches their Core 2 line of multicore processors
10/2007 | ARM launches their first multicore Cortex model (the quad core Cortex A9 MPcore)
Remark: Emergence of multi core processors

## Slide 145
3.4 Processors implementing the ARM v7 - ARM v8 ISA

## Slide 146: 3.4 Processors implementing the ARM v7 - ARM v8 ISA (1)
3.4 Processors implementing the ARMv7 - ARMv8 ISA
Processors implementing the ARMv7 or ARMv8 ISA are designated Cortex family
processors.
The Cortex-family along with its first member, the Cortex-M3 processor was
announced in 10/2004, without disclosing the ARMv7 ISA.
AMD revealed the technical specification of the ARMv7 ISA finally in 3/2005.
*

## Slide 147: 3.4 Processors implementing the ARM v7 - ARM v8 ISA (2)
The Cortex-A (application) profile
It aims at application processors for complex OS and user applications, like
processors in smartphones, tablets, netbooks, eBook readers etc.
Along with revealing the technical specifications for the ARMv7 ISA in 3/2005 ARM
introduced three family profiles to optimize its Cortex family processors for
specific market segments:
Profiles of ARM’s Cortex family [6], [7], [113]
The Cortex-A family supports a Virtual Memory System Architecture based on a
Memory Management Unit (MMU).
the A64 (AArch64),
the A32 (AArch32) and
the T32 (Thumb32)
instruction set.
It supports three instruction sets:
*

## Slide 148: 3.4 Processors implementing the ARM v7 - ARM v8 ISA (3)
The Cortex-R (Real-time) profile [113]
It marks embedded processors for real time applications, like mass storage or
printer controllers.
The Cortex-M (Microcontroller) profile [113]
Processors of the M profile are optimized for deeply embedded processors
aimed at microcontroller and cost sensitive applications, like automotive body
electronics, or smart sensors.
It implements a Protected Memory System Architecture (PMSA) based on a
Memory Protection Unit (MPU).
Supports the A32 and T32 instruction sets.
Supports writing interrupt handlers in high-level languages.
It implements a variant of the Protected Memory System Architecture (PMSA).
It supports a variant of the T32 instruction set.

## Slide 149: 3.4 Processors implementing the ARM v7 - ARM v8 ISA (4)
Extending the ARM Cortex family with the SecurCore profile in 10/2007
In 10/2007 ARM introduced the SecurCore profile.
It is optimized for smart card and secure applications.

## Slide 150: 3.4 Processors implementing the ARM v7 - ARM v8 ISA (5)
Recent ARM profiles
and processors [6]

## Slide 151: 3.4 Processors implementing the ARM v7 - ARM v8 ISA (5b)
According to the general scope of this Lecture Notes, subsequently we will be
concerned only with the Cortex-A series.
Remark

## Slide 152: 3.4 Processors implementing the ARM v7 - ARM v8 ISA (6)
Overview of the evolution of the Cortex-A series processors
In 2012 ARM expanded their Cortex family by processors implementing the
64-bit ARMv8 ISA, and subsequently
in 5/2017 AMD enhanced its ARMv8 ISA by the ARMv8.2 revision and introduced
first models implementing the new ISA release (the Cortex-A55 and Cortex-A75
models, as indicated below.
Cortex-A processors implementing
the ARMv7 ISA
Cortex-A processors
Cortex-A processors implementing
the ARMv8.0 ISA
32-bit architectures
(Announced in 2005)
Supporting big.LITTLE
core clusters
by specific models
64-bit architectures
(Announced in 2012)
Supporting big.LITTLE
core clusters
64-bit architectures
(Announced in 2017)
Supporting DynamIQ
core clusters
Cortex-A processors implementing
the ARMv8.2 ISA
Note
Subsequently, we designate the original ARMv8 ISA release as the ARMv8.0 ISA.
(Section 5)
(Will not discussed)
(Section 6)
(Will not detailed)
*

## Slide 153
4. Evolution of the Cortex-A series
ARMv7/v8.0 ISA-based models

## Slide 154: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (1)
Mainstream models
Low-power models
Performance classes of the Cortex-A series processors implementing the ARMv7/8.0 ISA
High-performance models
Performance classes in the Cortex-A processors (only ARMv7/8.0 ISA-based
processors) -1
Cortex-A15
Cortex-A57
Cortex-A72
Cortex-A73
Cortex-A8
Cortex-A9
(Cortex-A12)1
Cortex-A17
Cortex-A5
Cortex-A7
Cortex-A35
Cortex-A53
1The model Cortex-A-12 was introduced in 6/2013 but became withdrawn
in 10/2014 since its parameters were too close to that of the Cortex-A17, so
subsequently we will leave it out in most parts from our discussion.
4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models
*

## Slide 155: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (2)
2012
2013
10/2009
Cortex-A5
ARMv7
40 nm
High Performance
Mainstream
Low power
Announced
1
2
3
4
5
2006
2007
2008
2009
2010
2011
10/2011
Cortex-A7
ARMv7
28 nm
10/2012
Cortex-A53
ARMv8
20/16 nm
10/2005
Cortex-A8
ARMv7
65 nm
10/2007
Cortex-A9
ARMv7
40 nm
9/2010
Cortex-A15
ARMv7
32/28 nm
10/2012
Cortex-A57
ARMv8
20/16 nm
2014
2/2014
Cortex-A17
ARMv7
28 nm
6
7
DMIPS/MHz
2015
2/2015
Cortex-A72
ARMv8
16 nm
11/2015
Cortex-A35
ARMv8
16/14 nm
8
2016
5/2016
Cortex-A73
ARMv8
10 nm
6/2013
Cortex-A12
ARMv7
28 nm
Performance classes in the Cortex-A series
(only ARMv7/v8.0 ISA-based processors) -2
ARMv7
(32-bit)
ARMv8.0
(64-bit)

## Slide 156: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (3)
2012
2013
10/2009
Cortex-A5
ARMv7
40 nm
High Performance
Mainstream
Low power
Announced
1
2
3
4
5
2006
2007
2008
2009
2010
2011
10/2011
Cortex-A7
ARMv7
28 nm
10/2012
Cortex-A53
ARMv8
20/16 nm
10/2005
Cortex-A8
ARMv7
65 nm
10/2007
Cortex-A9
ARMv7
40 nm
9/2010
Cortex-A15
ARMv7
32/28 nm
10/2012
Cortex-A57
ARMv8
20/16 nm
2014
2/2014
Cortex-A17
ARMv7
28 nm
6
7
DMIPS/MHz
2015
2/2015
Cortex-A72
ARMv8
16 nm
11/2015
Cortex-A35
ARMv8
16/14 nm
8
2016
5/2016
Cortex-A73
ARMv8
10 nm
6/2013
Cortex-A12
ARMv7
28 nm
Three design teams working in parallel on Cortex-A processors []
http://www.anandtech.com/show/10347/arm-cortex-a73-artemis-unveiled
Austin (Texas) designs
Sophia-Antipolis (France) designs
Cambridge (UK) designs

## Slide 157: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (4)
"...The A15, A57, A72 all belong to the Austin family of microarchitectures, and as one would have guessed from the name, this is because they originated from ARM's Austin CPU design centre.
The A5, A7 and A53 belong to the Cambridge family while the Cortex A12, A17 and today's new A73 belong to the Sophia family, owning its name to the small city of Sophia-Antipolis which houses one of Europe's largest technology parks as well as ARM's French CPU design centre. Refering to their design location is however not enough to disambiguate microprocessor families, as we'll see completely new designs come out from each R&D center. In fact, this has already happened as the A12/17/73 can be seen as a new generation over the preceding the A9 microarchitecture and as such can be referred to as a "second generation Sophia family". This is an important notion to consider as in the future we'll be seeing completely new microarchitectures come out of ARM's various design teams."
Remarks on the designs of the Cortex-A series (taken from [99])
"The Cortex A73 being still in the same Sophia family effectively means the design is very much a 64-bit successor to the Cortex A17. The new core effectively inherits some of the main characteristics of its predecessor such as overall µarch philosophy as well as higher-level pipeline elements and machine width. And herein lies the biggest surprise of the Cortex A73 as a A72 successor: Instead of choosing to maintain A72’s 3-wide, or increase the microarchitecture’s decoder width, ARM opted to instead go back to a 2-wide decoder such as found on the current Sophia family. Yet the A73 positions itself a higher-performance and lower-power design compared to the larger A72."

## Slide 158
Addendum
The subsequent Cortex-A models were designed by the following teams:
The Cortex-A76 by the Sophia-Antipolis (France) team and
the Cortex A-55 by the Cambridge (UK) team.

## Slide 159: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (5)
Relative per core performance of Cortex-A processors with different
power budget [16]

## Slide 160: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (6)
Announced | Cortex-A model |  | DMIPS/MHz
10/2005 | Cortex-A8 |  | 2.0
10/2007 | Cortex-A9/A9 MPCore |  | 2.5
10/2009 | Cortex-A5/A5 MPCore |  | 1.6
9/2010 | Cortex-A15/A15 MPCore |  | 3.5-4.0
10/2011 | Cortex-A7 MP Core |  | 1.7
6/2013 | (Cortex-A12/A12 MPCore) |  | 3.0
2/2014 | Cortex-A17/A17 MPCore |  | 3.1-3.3
11/2015 | Cortex-A35 MPCore |  | ~ 2.1
10/2012 | Cortex-A53 MPCore |  | 2.3
10/2012 | Cortex-A57 MPCore |  | 4.1-4.7
2/2015 | Cortex-A72 MPCore |  | 6.3-7.35
5/2016 | Cortex-A73 MPCore |  | 7.4-8.5
Announcement dates and efficiency (DMIPS/MHz) of the Cortex-A models
implementing the ARMv7 and ARMv8.0 ISA
Source: ARM
DMIPS: Dhrystone MIPS (A synthetic benchmark that indicates integer performance)

## Slide 161: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (6b)
Per Generation
Cumulative
Pentium M Dothan
Core 2
Penryn
NHM (w/o SMT)
WSM
SNB
IVB
HSW
BRW
1.8
1.7
1.6
1.5
1.4
1.3
1.1
1.2
1
2
1.9
20%
18%
16%
14%
12%
10%
8%
6%
4%
2%
0%
24%
22%
SKL
Single thread IPC in Intel’s basic architectures (Based on [124])
Note that Intel raised IPC in the Core family only less then 2-times in about 10 years, whereas increased the efficiency of the Cortex-A line by more than 3-times.
*

## Slide 162: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (7)
Yearly shipment of ARM Cortex-A chips in different performance classes
(data from 2013) [13]

## Slide 163: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (8)
Target markets of the 64-bit Cortex-A series [49]

## Slide 164: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (9)
Support for big.LITTLE
configurations
Word length
of the models
Key features of ARMv7 - ARMv8.0 ISA based Cortex-A models
Multiprocessor
capability
Key features of ARMv7 - ARMv8.0 ISA based Cortex-A models
Inclusion of
L2 cache
(a)
(b)
(c)
(d)
*

## Slide 165: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (10)
a) Word length of the models
ARM’s 32-bit Cortex-A models
Word length of the models
ARM’s 64-bit Cortex-A models
Cortex-A models
implementing the ARMv7 ISA
Cortex-A53 (2012)
Cortex-A57 (2012)
Cortex-A35 (2015)
and subsequent models.
Cortex-A8 (2005)
Cortex-A9 (2007)
Cortex-A5 (2009)
Cortex-A15 (2010)
Cortex-A7 (2011)
Cortex-A17 (2014)
Cortex-A models
implementing the ARMv8 ISA
*

## Slide 166: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (11)
Optional L2 cache
Mandatory L2 cache
No L2 cache
Inclusion of an L2 cache
b) Inclusion of an L2 cache
Cortex-A5 (10/2009)
Cortex-A8 (10/2005)
Cortex-A9 (10/2007)
Cortex-A7 (10/2011)
Cortex-A15 (9/2010)
Cortex-A17 (2/2014)
All 64-bit models
*

## Slide 167: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (12)
Example for including an L2 cache : Eight-core A15-based high performance
cache coherent system [15]
Dynamic Memory Controller
Network
Interconnect
Network
Interconnect

## Slide 168: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (13)
A-priory
multiprocessor designs
Single processor designs,
no multiprocessor
capability
Dual designs with two options
Multiprocessor capability of the Cortex-A series implementing the ARMv7/v8.0 ISA
Cortex-A8 (2005)
Cortex-A5/Cortex-A5 MPCore (2009)
Cortex-A9/Cortex-A9 MPCore (2007)
(Cortex-A12/Cortex-A12 MPCore (2013))1
Cortex-A15/Cortex-A15 MPCore (2010)
Cortex-A17/Cortex-A17 MPCore (2014)
Cortex-A7 MPCore (2011)
All 64-bit models
(from 2012 on)
a single processor option and
a multiprocessor capable option
c) Multiprocessor capability
Here we note that in figures or tables we often omit the MPCore tag for the sake
of brevity.
1The model Cortex-A12 was introduced in 6/2013 but became withdrawn
in 10/2014 since its parameters were too close to that of the Cortex-A17, so
subsequently we will leave it out in most parts from our discussion.
*

## Slide 169: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (14)
Remarks on the interpretation of the term MPCore by ARM
ARM introduced the term MPCore in connection with the announcement of the
ARM11 MPCore in 2004 despite the fact that the ARM11 MPCore was actually
a multicore processor including up to 4 cores rather than a multiprocessor.
Since then MPCore indicates the multiprocessor capability of the processor.
ARM Cortex-A9 it does not support multiprocessor configurations and
ARM Cortex-A9 MPCore it supports multiprocessor configurations.
Along with the ARM Cortex-A9 MPCore (2007) ARM re-interpreted this term.
The ARM Cortex-A9 introduced 1-4 cores and it had two alternatives

## Slide 170: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (15)
No support for big.LITTLE
configurations
Support of big.LITTLE configuraions
Support for big.LITTLE
configurations
First 32-bit (ARMv7) models, such as the
Cortex-A8 (2005)
Cortex-A9 (2007)
Cortex-A5 (2009)
Advanced 32-bit (ARMv7) models, such as the
Cortex-A15 (2010)
Cortex-A7 (2011)
Cortex-A17 (2014)
and all 64-bit (ARMv8) models
d) Support for big.LITTLE configurations
ARM revealed the big.LITTLE technology in a White Paper, in 09/2011.
Accordingly, ARM began supporting the big.LITTLE technology along with their
advanced 32-bit (ARMv7) designs, as shown below.
*

## Slide 171: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (16)
CPU Core | Architecture | Efficiency | big.LITTLE | Announced | Available in devices | Target
Cortex-A17 | ARMv7 (32-bit) | 4,0 DMIPS/MHz | Yes (with A7) | 2014 | 2015 | Mainstream
Cortex-A15 | ARMv7 (32-bit) | 4,0 DMIPS/MHz | Yes (with A7) | 2010 | Q2/2013 | High-end
(Cortex-A12 | ARMv7 (32-bit) | 3,0 DMIPS/MHz | -- | 2013 | H2/2015 | Mainstream)
Cortex-A9 | ARMv7 (32-bit) | 2,5 DMIPS/MHz | -- | 2007 | 2010 | Mainstream
Cortex-A8 | ARMv7 (32-bit) | 2,0 DMIPS/MHz | -- | 2005 | 2009 | Mainstream
Cortex-A7 | ARMv7 (32-bit) | 1,9 DMIPS/MHz | Yes (A15/A17) | 2011 | 2012 | Low power
Cortex-A5 | ARMv7 (32-bit) | 1,6 DMIPS/MHz | -- | 2009 | 2011 | Low power
Main features of the Cortex A series implementing the ARMv7 ISA [51]

## Slide 172: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (17)
CPU Core | Architecture | Efficiency | big.LITTLE | Announced | Available in devices | Target
Cortex-A73 | ARMv8 (64-bit) | 7.4-8.5 DMIPS/MHz | Yes (with A53/A35) | 2016 | 2017 | High-end
Cortex-A72 | ARMv8 (64-bit) | 6.3-7.3 DMIPS/MHz | Yes (with A53/A35) | 2015 | 2016 | High-end
Cortex-A57 | ARMv8 (64-bit) | 4,8 DMIPS/MHz | Yes (with A53) | 2012 | 2015 | High-end
Cortex-A53 | ARMv8 (64-bit) | 2,3 DMIPS/MHz | Yes (with A57) | 2012 | H2/2014 | Low power
Cortex-A35 | ARMv8 (64-bit) | 2,1 DMIPS/MHz | Yes (with A57/A72) | 2015 | H2/2016 | Low power
Main features of the Cortex A series implementing the ARMv8.0 ISA [51]

## Slide 173: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (17b)
CPU Core | Architecture | Efficiency | big.LITTLE | Announced | Available in devices | Target
Cortex-A76 | ARMv8 (64-bit) | ~10.7-12.4 DMIPS/MHz | Yes (with A55) | 2018 | 2018 | High-end
Cortex-A75 | ARMv8 (64-bit) | ~8.2-9.5 DMIPS/MHz | Yes (with A55) | 2017 | 2018 | High-end
Cortex-A55 | ARMv8 (64-bit) | ~3 DMIPS/MHz | Yes (with A75/A76) | 2017 | 2018 | Low-end
Main features of the Cortex A series implementing the ARMv8.2 ISA [51]

## Slide 174
High performance
Mainstream
Low power
Key features of ARMv7 ISA based microarchitectures (based on [14])

## Slide 175
Low power
High performance
Key features of ARMv8.0 ISA based microarchitectures (based on [14])

## Slide 176
High performance
Low power
Key features of ARMv8.2 ISA based microarchitectures (based on [14])

## Slide 177: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (20)
Relative performance, efficiency and power efficiency of subsequent models
of the Cortex-A series [99]
2007
2016

## Slide 178: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (21)
Performance comparison: ARM’s Cortex-A72 vs. Intel’s Core-M [72]

## Slide 179: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (22)
Die area requirement of different applications [17]

## Slide 180: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (23)
Wide configuration options - Example: The 64-bit low power Cortex-A35
It is a widely configurable application processor, as indicated below.
Figure: Configuration options of the Cortex-A35 [77]
It is configurable for applications ranging from mobiles to deeply embedded.
Target consumption is below 125 mW.
On 28 nm technology it achieves 1 GHz by 90 mW, for planned smaller feature
sizes of 14/16 nm ARM expects less consumption.

## Slide 181: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (24)
Up to 48 core server SoC based on the CoreLink CCN-512 interconnect [72]

## Slide 182: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (25)
 | (SOC) System- On-a-Chip | Notable Product(s) Containing | ARM Cortex-A model | No. of Cores
Apple | A4 | iPhone 4, iPod Touch (4th Gen), iPad (1st Gen), AppleTV (2nd Gen) | Cortex-A8 | 1
 | A5 | iPhone 4S, iPad 2, AppleTV (3rd Gen) | Cortex-A9 | 2
 | A5X | iPad (3rd Gen, Retina Display) | Cortex-A9 | 2
Samsung | Exynos 3 Single | Samsung Galaxy S, Samsung Galaxy Nexus S, | Cortex-A8 | 1
 | Exynos 4 Dual | Samsung Galaxy SII, Samsung Galaxy Note (International) | Cortex-A9 | 2
 | Exynos 4 Quad | Samsung Galaxy SIII | Cortex-A9 | 4
 | Exynos 5 Dual | Chrombook | Cortex-A15 | 2
Nvidia | Tegra | Microsoft Zune HD | (ARM11) | 1
 | Tegra 2 | ASUS Eee Pad Transformer, Samsung Galaxy Tab 10.1, Motorola Xoom, Dell Streak 7 & Pro, Sony Tablet S | Cortex-A9 | 2
 | Tegra 3 | ASUS Transformer Pad 300, ASUS Nexus 7, Acer Iconia Tab A510 & A700, HTC One X | Cortex-A9 | 4
Qualcomm | Snapdragon S1 | Large number of devices | (ARM11)/A5 | 1
Texas Instruments | OMAP 3 | Barnes and Noble Nook Color | Cortex-A8 | 1
 | OMAP 4 | Amazon Kindle Fire, Samsung Galaxy Tab 2, Blackberry Playbook, Samsung Galaxy Nexus, Barnes and Noble Nook Tablet | Cortex-A9 | 2
 | OMAP 5 | N/A | Cortex-A15 | 2
Use of ARMv7-based (32-bit) ARM Cortex-A models in mobiles [18]

## Slide 183: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (26)
Total number of ARM chips shipped [19]
SBSA: Server Base System Architecture, it is a standardized platform for servers built on 64-bit
ARM processors

## Slide 184: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (27)
"The Cortex A9 was an incredibly important design for ARM as, in my view, it provided the corner-stone for SoC and device vendors to create some of the designs that powered some of the most successful devices that brought with them a turning-point in smartphone performance and experience. Apple’s A5, Samsung’s Exynos 4210/4412, and TI OMAP4430/4460 were all SoCs which made the A9 a very successful CPU micro-architecture.
Following the Cortex A9 we saw the introduction of the Cortex A15. The core was a substantial jump in terms of performance as it provided the single largest IPC improvement in ARM’s Cortex A-profile of application processors. While the A15 represented a large performance boost, it came at significant cost in terms of power efficiency and overall power usage. It took some time for the Cortex A15 to establish itself in the mobile space as the first designs such as the Exynos 5250 and 5410 failed to impress due to bad power efficiency due to various issues.
It’s at this point where ARM introduced big.LITTLE with the argument that one can have the best of both worlds, a high-power performant core together with a low-power high-efficiency core. It was not until late 2014 and 2015 did we finally see some acceptable implementations of A15 big.LITTLE solutions such as the Kirin 920 or Exynos 5422."
Remarks on the evolution of the Cortex-A series (taken from [99]) -1
There is a brief but essential description of ARM's Cortex series in [99]. Due to its
relevance in the following we will cite parts of it.

## Slide 185: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (28)
"The Cortex A57 succeeded the Cortex A15 and was ARM’s first “big” core to employ ARMv8 64-bit ISA. Accompanied by the high-efficiency Cortex A53 cores this represented an important shift not unlike the x86-64 introduction in the desktop PC space well over a decade before. The cores came at a moment where the industry was still at shock of Apple’s introduction of the A7 SoC and Cyclone CPU micro-architecture, beating ARM in terms delivering the first 64-bit ARMv8 silicon. Suddenly everybody in the industry was playing catch-up in trying to bring their own 64-bit products as it was seen as an absolutely required feature-check to remain competitive.
This pressured shift to 64-bit was in my view a crippling blow to many 2015’s SoCs as it forced vendors into employing sub-optimal Cortex A57 and A53 designs. HiSilicon and MediaTek saw an actual regression in performance as flagship SoCs such as the Kirin 930 and Helio X10 had to make due with only A53 cores for performance as they decided against employing A57 cores due to power consumption concerns. The Kirin 930 or the X10 were in effect slower chipsets than their predecessors. Only Samsung was fairly successful in releasing reasonable designs such as the Exynos 5433 and Exynos 7420 – yet these had respectively regressed or barely improved in terms of power efficiency when compared to mature Cortex A15 implementations such as the Exynos 5430. Then of course we had sort of a lost generation of devices due to Qualcomm’s unsuccessful Snapdragon 810 and 808 SoCs, a topic we’ll eventually revisit in our deep dive of the Snapdragon 820 and Exynos 8890."
Remarks on the evolution of the Cortex-A series (taken from [99]) -2

## Slide 186: 4. Evolution of the Cortex-A series ARMv7/v8.0 ISA-based models (29)
"Some readers will notice I left out the Cortex A12 and A17 – and I did that on purpose in trying to get to my point. The Cortex A12 was unveiled in July 2013 and presented as a successor to the Cortex A9. The core had a relatively short lifetime as it was quickly replaced within 6 months with the Cortex A17 in February 2014 which improved performance and also made the core big.LITTLE compatible with the Cortex A7. The Cortex A17 saw limited adoption in the mobile space. In fact, among the few SoCs such as Rockchip’s RK3288 and some little known chips such as HiSilicon’s Hi3536 multimedia SoC, it was only MediaTek’s MT6595 that saw moderate success in design wins such as Meizu’s MX4.
Remarks on the evolution of the Cortex-A series (taken from [99]) -3

## Slide 187
5. Cortex-A models based on the ARMv8.0 ISA
5.2 High performance Cortex-A models based on the
ARMv8.0 ISA
5.3 Low-power Cortex- A models based on the
ARMv8.0 ISA
(This Section will not be discussed)
5.1 Overview of the Cortex-A models based on the
ARMv8.0 ISA

## Slide 188
5.1 Overview of the Cortex-A models based on the ARMv8.0 ISA

## Slide 189: 5.1 Overview of the Cortex-a models based on the ARMv8.0 ISA (1)
ARMv4
ARMv5
ARMv6
ARMv8.0-A
ARMv7-A/R
Jazelle
(Jazelle DBX)
VFPv1/2
Thumb
(ARMv4T)
SIMD
TrustZone
Thumb-2
(ARMv6T2)
Adv. SIMD1
(NEON)
VFPv3/v42
Crypto-graphy ext.
Jazelle
(ex. by SW)
Jazelle RCT3
(ThumbEE)
ARM710T
(~1995)
ARM926
(2001)
ARM1176
(2004)
Cortex-A5 - A15
(2005)
Cortex-A53/A57
(2012)
Examples
To reduce
code size
SVE4
To enhance
compute
capabilities
AArch32
AArch64
Remarks: See on the slide 2.1 Overview (5).
To speed up
the execution
of bytecodes
To enhance
security
5.1 Overview of Cortex-A models based on the ARMv8.0 ISA -1 (After [64])
10/2011 ARM disclosed the 64-bit ARMv8 architecture
with enhancements as indicated in the Figure below
and discussed in Section 2.

## Slide 190: 5.1 Overview of the Cortex-a models based on the ARMv8.0 ISA (2)
High performance
ARMv8.0 ISA-based
(64-bit) Cortex-A models
ARMv8.0 ISA-based (64-bit) Cortex A models
Mainstream
ARMv8.0 ISA-based
(64-bit) Cortex-A models
Low power
ARMv8.0 ISA-based
(64-bit) Cortex-A models
Cortex-A57 (2012)
Cortex-A72 (2015)
Cortex-A73 (2016)
Cortex-A53 (2012)
Cortex-A35 (2015)
Cortex-A32 (2016)
Section 5.2
Section 5.3
No announcement yet
10/2012: ARM announced the 64-bit high performance Cortex-A-57 and the
low power Cortex-A-53 processors, as first implementations of the ARMv8
architecture, with immediate availability.
02/2015 ARM extended their 64-bit Cortex-A series by the high performance
Cortex-A72 model, and in 11/2015 by the low power Cortex-A35, as shown
below.
05/2016 ARM extended the 64-bit Cortex-A series by the high performance
Cortex-A73 model.
5.1 Overview of the Cortex-a models based on the ARMv8.0 ISA -2

## Slide 191: 5.1 Overview of the Cortex-a models based on the ARMv8.0 ISA (3)
2012
2013
10/2009
Cortex-A5
ARMv7
40 nm
High Performance
Mainstream
Low power
Announced
1
2
3
4
5
2006
2007
2008
2009
2010
2011
10/2011
Cortex-A7
ARMv7
28 nm
10/2012
Cortex-A53
ARMv8
20/16 nm
10/2005
Cortex-A8
ARMv7
65 nm
10/2007
Cortex-A9
ARMv7
40 nm
9/2010
Cortex-A15
ARMv7
32/28 nm
10/2012
Cortex-A57
ARMv8
20/16 nm
2014
2/2014
Cortex-A17
ARMv7
28 nm
6
7
DMIPS/MHz
2015
2/2015
Cortex-A72
ARMv8
16 nm
11/2015
Cortex-A35
ARMv8
16/14 nm
8
2016
5/2016
Cortex-A73
ARMv8
10 nm
6/2013
Cortex-A12
ARMv7
28 nm
5.1 Overview of the Cortex-A models based on the ARMv8.0 ISA -3

## Slide 192
5.2 High performance Cortex-A models based on the ARMv8.0 ISA
5.2.1 The high performance Cortex-A57
5.2.2 The high performance Cortex-A72
5.2.3 The high performance Cortex-A73

## Slide 193
5.2.1 The high performance Cortex-A57

## Slide 194: 5.2.1 The high performance Cortex-A57 (1)
2012
2013
10/2009
Cortex-A5
ARMv7
40 nm
High Performance
Mainstream
Low power
Announced
1
2
3
4
5
2006
2007
2008
2009
2010
2011
10/2011
Cortex-A7
ARMv7
28 nm
10/2012
Cortex-A53
ARMv8
20/16 nm
10/2005
Cortex-A8
ARMv7
65 nm
10/2007
Cortex-A9
ARMv7
40 nm
9/2010
Cortex-A15
ARMv7
32/28 nm
10/2012
Cortex-A57
ARMv8
20/16 nm
2014
2/2014
Cortex-A17
ARMv7
28 nm
6
7
DMIPS/MHz
2015
2/2015
Cortex-A72
ARMv8
16 nm
11/2015
Cortex-A35
ARMv8
16/14 nm
8
2016
5/2016
Cortex-A73
ARMv8
10 nm
6/2013
Cortex-A12
ARMv7
28 nm
5.2.1 The high performance Cortex-A57 -1 (based on [12])

## Slide 195: 5.2.1 The high performance Cortex-A57 (2)
10/2012: Announced along with the low power Cortex-A53 processor, with
immediate availability for licensing.
2014: First mobile devices with Cortex-A57 models are emerged.
They are 64-bit successors to the high performance 32-bit Cortex A15.
The A57 and A53 models can be used either as stand alone processors or
as components of a big-LITTLE configuration, similar to the 32-bit
Cortex-A15/A7 combination.
Interoperability with the ARM Mali GPU family is provided.
Target process technology: 16 or 20 nm.
The high performance Cortex-A57 -2

## Slide 196: 5.2.1 The high performance Cortex-A57 (3)
Key features of the microarchitecture of the Cortex-A57
Full compatible with the preceding ARMv7 32-bit ISA.
Integrated L2 cache of 512 kB to 2 MB.
Up to 4 Cortex-A57 CPUs that execute the ARMv8 64-bit ISA.
Remarks
AMBA: Advanced Microcontroller Bus Architecture
(On-chip bus standard for SoC) designs
128-bit AMBA ACE coherent interface for connecting multiple (up to 4)
Cortex-A57 processors.
Processor wide cache coherence supported by a Snoop Control Unit (SCU).

## Slide 197: 5.2.1 The high performance Cortex-A57 (4)
High level block diagram of the Cortex-A57 [53]
PA: Physical Address
DED: Double Error Detection
ECC: Error Correcting Code
ACP: Accelerator Coherence Port
(to connect non-cached
coherent data sources)
SCU: Snoop Control Unit
AMBA: Advanced Microcontroller
Bus Architecture
(On-chip bus standard for
SoC) designs)
ACE: AXI Coherency Extensions
(Used in big.LITTLE systems
for smartphones, tablets,
etc.)

## Slide 198: 5.2.1 The high performance Cortex-A57 (5)
APB
ATB
Interrupts
Main functional blocks of the high performance Cortex-A57 CPU [74]

## Slide 199: 5.2.1 The high performance Cortex-A57 (6)
Remarks: Non trivial abbreviations in the above Figure
ATB: AMBA Trace Bus
APB: Advanced Peripheral Bus
ACP: Accelerator Coherence Port
(to connect non-cached coherent data sources)
ACE: AXI Coherency Extensions
(Used in big.LITTLE systems for smartphones, tablets, etc.)
AXI: Advanced eXtensible Interface
(The most widespread AMBA interface).

## Slide 200: 5.2.1 The high performance Cortex-A57 (7)
Key features of the microarchitecture of the Cortex-A57 core -1
Each core fetches four instructions per cycle from the Icache,
decodes and renames three microinstructions per cycle,
dispatches three microinstructions per cycle to the issue queues,
whereas the issue queues issue up to eight microinstructions per cycle
to the eight available execution units.
The available execution units are
a branch unit
dual single cycle integer units
a multi-cycle integer MAC/DIV/CRC unit
dual Advanced SIMD (NEON)/FP. Crypto units and
dual load/store units.

## Slide 201: 5.2.1 The high performance Cortex-A57 (8)
Core efficiency: 4.8 DMIPS/MHz
Expected core frequency up to 2.5 GHz in a 16 nm process implementation.
Key features of the microarchitecture of the Cortex-A57 core -2

## Slide 202: 5.2.1 The high performance Cortex-A57 (9)
Pipeline of the Cortex-A57 core -1
The Cortex-A57 core has a 3-wide in-order front end and an 8 issue-wide out-of-
order back end pipeline with 15 stages for integer processing and additional
pipeline stages for NEON and FP processing, as indicated in the next two
Figures.

## Slide 203: 5.2.1 The high performance Cortex-A57 (10)
Contrasting the Cortex-A53 and Cortex-A57 arithmetic pipelines
[Based on 54]
D: Decode
R: Rename
P: Dispatch
I: Issue
E: Execute
WB: Write Back
Notes: a) Branch and Load/Store pipelines not shown
(1x Load/Store pipeline for the Cortex A-53 and
2x Load/Store and 1x Branch pipeline for the Cortex-A-57)
b) For the A57 only one Complex Cluster pipeline shown
from the two available (these are actually ASIMD pipes)

## Slide 204: 5.2.1 The high performance Cortex-A57 (10b)
Pipeline structure of a Cortex-A57 core, as shown in the Cortex-A57
Software Optimization Guide [122]

## Slide 205: 5.2.1 The high performance Cortex-A57 (10c)
Operation of ASIMD (advanced SIMD) pipelines [123]
ASIMD multiply-accumulate pipelines support late-forwarding of accumulate
operands from similar μops in order to speed up the execution of a typical
sequence of FP multiply-accumulate instructions, as detailed next.
Actually, in order to issue an FMAD operation not all three input operands need
to be ready.
The FMAD operation can already be started when the multiply operands are
available, the accumulate operand can be added later after the multiply
operation has already been calculated.
This kind of execution of FMA operations is called late-forwarding.
ASIMD is beneficial, when a chain of FMAD operations needs to be executed
such that one FMA is using the result of the previous FMA operation as its
accumulate operand.
FMAD operations last 9 cycles, thus without ASIMD 9 cycles need to be waited
before the next FMAD can be issued on the pipe.
But with late forwarding the next FMAD can be issued already in the 4th cycle,
as by the time the FMAD needs the accumulate operand the previous FMAD
would already be finished.
All in all FSIMD allows the interleaved execution of a chain of FMAD operations
significantly faster than without this capability.

## Slide 206: 5.2.1 The high performance Cortex-A57 (10d)
Execute latencies of FMADD instructions with and without ASIMD capability
[122]

## Slide 207: 5.2.1 The high performance Cortex-A57 (10e)
Implementation of ASIMD pipelines in subsequent ARM processors
The ASIMD capability of the A57 processors was officially disclosed in the
Software Optimization Guide of this processor only in 01/2015, many years
after its introduction (10/2012).
According to the available documentation, the high-performance models
implementing the ARM8 ISA (Cortex-A57/72/73 etc.) provide this feature
whereas the low-performance models, like the Cortex-A53 etc. not).

## Slide 208: 5.2.1 The high performance Cortex-A57 (11)
Actual pipeline structure of the Cortex-A57 core (alternative view) [71]

## Slide 209: 5.2.1 The high performance Cortex-A57 (12)
Cortex-A57/A53 performance - compared to the Cortex-A15 [55]

## Slide 210: 5.2.1 The high performance Cortex-A57 (13)
Example: A Cortex-A57/Cortex-A53 big.LITTLE system [52]

## Slide 211
5.2.2 The high performance Cortex-A72

## Slide 212: 5.2.2 The high performance Cortex-A72 (1)
5.2.2 The high performance Cortex-A72 (1) (based on [12])
2012
2013
10/2009
Cortex-A5
ARMv7
40 nm
High Performance
Mainstream
Low power
Announced
1
2
3
4
5
2006
2007
2008
2009
2010
2011
10/2011
Cortex-A7
ARMv7
28 nm
10/2012
Cortex-A53
ARMv8
20/16 nm
10/2005
Cortex-A8
ARMv7
65 nm
10/2007
Cortex-A9
ARMv7
40 nm
9/2010
Cortex-A15
ARMv7
32/28 nm
10/2012
Cortex-A57
ARMv8
20/16 nm
2014
2/2014
Cortex-A17
ARMv7
28 nm
6
7
DMIPS/MHz
2015
2/2015
Cortex-A72
ARMv8
16 nm
11/2015
Cortex-A35
ARMv8
16/14 nm
8
2016
5/2016
Cortex-A73
ARMv8
10 nm
6/2013
Cortex-A12
ARMv7
28 nm

## Slide 213: 5.2.2 The high performance Cortex-A72 (2)
02/2015: Announced along with the CoreLink CCI-500 cache Cache Coherent
Interconnect and the Mali T880 GPU with immediate availability for licensing.
Q1/2016: First premium level mobile devices with Cortex-A72.
The Cortex-A72 is based on the high performance 64-bit Cortex-A57.
Nevertheless, every logical block of the Cortex-A57 was optimized for
power efficiency.
It was designed in ARM's Austin, Texas design center.
The Cortex-A72 can be used either as stand alone processors or as part of
a big-LITTLE configuration along with the Cortex-A53 processors.
Interoperability with the ARM Mali GPU family.
Target process technology: 16 nm FinFET technology.
The high performance Cortex-A72 -2 [91]

## Slide 214: 5.2.2 The high performance Cortex-A72 (3)
Sustained relative performance of high performance Cortex-a models
within a given power budget [91]
http://www.anandtech.com/show/9184/arm-reveals-cortex-a72-architecture-details

## Slide 215: 5.2.2 The high performance Cortex-A72 (4)
Energy consumption of high performance Cortex-A models for the same
workload [91]

## Slide 216: 5.2.2 The high performance Cortex-A72 (5)
ECC: Error Correcting Code
ACP: Accelerator Coherence Port
(to connect non-cached
coherent data sources)
SCU: Snoop Control Unit
(Provides coherence within the
the processor)
AMBA: Advanced Microcontroller
Bus Architecture
(On-chip bus standard for
SoC) designs)
ACE: AXI Coherency Extensions
AMBA4 cache coherent interface
(Used in big.LITTLE systems
for smartphones, tablets,
etc.)
CHI: Coherent Hub Interface
(AMBA5 Cache coherent
interface used in servers)
High level block diagram of the Cortex-A72 [91]

## Slide 217: 5.2.2 The high performance Cortex-A72 (6)
Key features of the microarchitecture of the Cortex-A72 [91]
It has a three-wide out-of-order front-end and a five-wide out-of-order back-end,
as seen in the next Figure.
Integrated L2 cache of 512 kB to 4 MB.
Up to 4 Cortex-A73 CPUs executing the ARMv8 64-bit ISA.
Remarks
AMBA: Advanced Microcontroller Bus Architecture
(On-chip bus standard for SoC) designs
128-bit coherent AMBA4 ACE or AMBA5 CHI interface for connecting multiple
(up to 4) Cortex-A57 processors and further system components.
Processor wide cache coherence supported by a Snoop Control Unit (SCU).
Significant improvements in power efficiency through optimizing every block
of the Cortex-A57.

## Slide 218: 5.2.2 The high performance Cortex-A72 (7)
Pipeline structure of the high-end Cortex-A72 [92]

## Slide 219: 5.2.2 The high performance Cortex-A72 (8)
More detailed block diagram of the high performance Cortex-A72 [95]

## Slide 220: 5.2.2 The high performance Cortex-A72 (9)
Remark
A detailed description of the microarchitecture of the Cortex-A72 can be found in [91].

## Slide 221
5.2.3 The high performance Cortex-A73

## Slide 222: 5.2.3 The high performance Cortex-A73 (1)
5.2.3 The high performance Cortex-A73 (1) (based on [12])
2012
2013
10/2009
Cortex-A5
ARMv7
40 nm
High Performance
Mainstream
Low power
Announced
1
2
3
4
5
2006
2007
2008
2009
2010
2011
10/2011
Cortex-A7
ARMv7
28 nm
10/2012
Cortex-A53
ARMv8
20/16 nm
10/2005
Cortex-A8
ARMv7
65 nm
10/2007
Cortex-A9
ARMv7
40 nm
9/2010
Cortex-A15
ARMv7
32/28 nm
10/2012
Cortex-A57
ARMv8
20/16 nm
2014
2/2014
Cortex-A17
ARMv7
28 nm
6
7
DMIPS/MHz
2015
2/2015
Cortex-A72
ARMv8
16 nm
11/2015
Cortex-A35
ARMv8
16/14 nm
8
2016
5/2016
Cortex-A73
ARMv8
10 nm
6/2013
Cortex-A12
ARMv7
28 nm

## Slide 223: 5.2.3 The high performance Cortex-A73 (2)
05/2016: Announced along with the G71 graphics processor with immediate
availability for licensing.
First premium level mobile devices with Cortex-A73 in 2017.
The Cortex-A73 is successor to the high performance 64-bit Cortex-A72.
But whereas the Cortex-A72 was designed in Austin, Texas, the Cortex-A73
is a designed from scatch by a French team in Sophia-Antipolis design park.
The design started in 2013 inspired by the mainstream Cortex-A17.
The Cortex-A73 can be used either as stand alone processors or as part of
a big-LITTLE configuration along sith the Cortex-a53/A35 processors.
Interoperability with the ARM Mali GPU family is provided.
Target process technology: 10 nm FinFET technology.
The high performance Cortex-A73 -2 [92]

## Slide 224: 5.2.3 The high performance Cortex-A73 (3)
Relative performance, efficiency and power efficiency of subsequent models
of the Cortex-A line [92]
2007

## Slide 225: 5.2.3 The high performance Cortex-A73 (4)
Cortex-A73 performance improvement over the Cortex-A72 [92]

## Slide 226: 5.2.3 The high performance Cortex-A73 (5)
Cortex-A73 power reduction over the Cortex-A72 [92]

## Slide 227: 5.2.3 The high performance Cortex-A73 (6)
Cortex-A73 performance improvement in a big-LITTE configuration [92]

## Slide 228: 5.2.3 The high performance Cortex-A73 (7)
ECC: Error Correcting Code
ACP: Accelerator Coherence Port
(to connect non-cached
coherent data sources)
SCU: Snoop Control Unit
(Provides coherence within the
the processor)
AMBA: Advanced Microcontroller
Bus Architecture
(On-chip bus standard for
SoC) designs)
AXI4: Advanced eXtensible Interface
(The most widespread AMBA4
non cache-coherent interface)
ACE: AXI Coherency Extensions
AMBA4 cache coherent interface
(Used in big.LITTLE systems
for smartphones, tablets,
etc.).
High level block diagram of the Cortex-A73 [93]

## Slide 229: 5.2.3 The high performance Cortex-A73 (8)
Key features of the microarchitecture of the Cortex-A73 [92]
It has a two-wide out-of-order front-end and a four-wide out-of-order back-end.
This is in contrast to the Cortex-A72 that has a three-wide in-order front-end
and a five-wide out-of-order back-end (see subsequent Figures).
Integrated L2 cache of 256 kB to 8 MB.
Up to 4 Cortex-A73 CPUs executing the ARMv8 64-bit ISA.
Remarks
AMBA: Advanced Microcontroller Bus Architecture
(On-chip bus standard for SoC) designs
128-bit AMBA AXI4 non-coherent or ACE coherent interface for connecting
multiple (up to 4) Cortex-A57 processors and further system components.
Processor wide cache coherence supported by a Snoop Control Unit (SCU).

## Slide 230: 5.2.3 The high performance Cortex-A73 (9)
Pipeline structure of the high-end Cortex-A73 [92]

## Slide 231: 5.2.3 The high performance Cortex-A73 (10)
By contrast: Pipeline structure of the high-end Cortex-A72 [92]

## Slide 232: 5.2.3 The high performance Cortex-A73 (11)
Key differences in the pipeline structure of the Cortex-A73 and -A72 [92]
The Cortex-A73 has a shorter pipeline than the -A72 (11+ stages vs. 14+ stages).
The Cortex-A73 has a smaller front-end than the -A72 (a dual-issue out-of-order
front-end vs. a three issue out-of-order front-end).
The Cortex-A73 has also a smaller back-end than the -A72 (four-wide out-of order
back-end with an issue rate of 7 vs. a five-wide out-of order back-end with an
issue-rate of 10).
Still the Cortex-A73 has a higher efficiency (7.4-8.5 DMIPS/MHz vs. 6.3-7.35
DMIPS/MHz), achieved through a superior design.

## Slide 233: 5.2.3 The high performance Cortex-A73 (12)
Die size reduction in ARM's high-performance 64-bit processor line [92]

## Slide 234: 5.2.3 The high performance Cortex-A73 (13)
Range of scalability of the Cortex-A73 processor [92]

## Slide 235: 5.2.3 The high performance Cortex-A73 (14)
Remark
A detailed description of the microarchitecture of the cortex-A73 can be found in [92].

## Slide 236
5. 3 The low power Cortex-A models based on the ARMv8.0 ISA
5.3.1 The low power Cortex-A53
5.3.2 The low power Cortex-A35

## Slide 237
5.3.1 The low power Cortex-A53

## Slide 238: 5.3.1 The low power Cortex-A53 (1)
5.3.1 The low power Cortex-A53 -1 (based on [12])
2012
2013
10/2009
Cortex-A5
ARMv7
40 nm
High Performance
Mainstream
Low power
Announced
1
2
3
4
5
2006
2007
2008
2009
2010
2011
10/2011
Cortex-A7
ARMv7
28 nm
10/2012
Cortex-A53
ARMv8
20/16 nm
10/2005
Cortex-A8
ARMv7
65 nm
10/2007
Cortex-A9
ARMv7
40 nm
9/2010
Cortex-A15
ARMv7
32/28 nm
10/2012
Cortex-A57
ARMv8
20/16 nm
2014
2/2014
Cortex-A17
ARMv7
28 nm
6
7
DMIPS/MHz
2015
2/2015
Cortex-A72
ARMv8
16 nm
11/2015
Cortex-A35
ARMv8
16/14 nm
8
2016
5/2016
Cortex-A73
ARMv8
10 nm
6/2013
Cortex-A12
ARMv7
28 nm

## Slide 239: 5.3.1 The low power Cortex-A53 (2)
10/2012: Announced along with the performance oriented Cortex-A57 processor,
with immediate availability for licensing.
2014: First mobile devices with the Cortex-A53.
It is the 64-bit successor to the Cortex-A7.
The A57 and A53 models can be used either as stand alone processors or
as components in a big-LITTLE configuration, similar to the 32-bit Cortex-A15
and A7 models.
Target process technology: 16 or 20 nm.
The low power Cortex-A53 -2 [75]

## Slide 240: 5.3.1 The low power Cortex-A53 (3)
High level block diagram of the Cortex-A53 [53]
PA: Physical Address
ECC: Error Correcting Code
ACP: Accelerator Coherence Port
(to connect non-cached
coherent data sources)
SCU: Snoop Control Unit
AMBA: Advanced Microcontroller
Bus Architecture
(On-chip bus standard for
SoC) designs)
ACE: AXI Coherency Extensions
AMBA4 cache coherent interface
(Used in big.LITTLE systems
for smartphones, tablets,
etc.)

## Slide 241: 5.3.1 The low power Cortex-A53 (4)
Key features of the microarchitecture of the Cortex-A53 core -1
Fully compatible with the preceding ARMv7 32-bit ISA.
Integrated L2 cache of 128 kB to 2 MB.
Up to 4 Cortex-A53 CPU cores that execute the ARMv8 64-bit ISA.
Remarks
AMBA: Advanced Microcontroller Bus Architecture
(On-chip bus standard for SoC) designs
128-bit AMBA coherent interface for connecting multiple (up to 4)
Cortex-A53 processors.
Processor wide cache coherence supported by a Snoop Control Unit (SCU).

## Slide 242: 5.3.1 The low power Cortex-A53 (5)
Key features of the microarchitecture of the Cortex-A53 core -2
The Cortex-A53 core has a dual-issue in-order pipeline actually with 5 individual
pipelines constituting the back end, as indicated in the next Figure.
The pipeline for integer processing has 8 pipeline stages, NEON and FP
processing has two additional pipeline stages, as seen in the Figure above.
Dual
Integer
Fetch
Figure: Pipeline stages of the Cortex-A53 [76]

## Slide 243: 5.3.1 The low power Cortex-A53 (6)
ARM CPU Core Comparison |  | 
 | Cortex-A7 | Cortex-A53
ARM ISA | ARMv7 (32-bit) | ARMv8 (32/64-bit)
Issue Width | Partially 2 micro-ops | 2 micro-ops
Pipeline Length | 8 | 8
Integer Add units | 2 | 2
Integer Mul unit | 1 | 1
Load/Store Units | 1 | 1
Branch Unit | 1 | 1
FP/NEON ALU | 1x64-bit | 1x64-bit
L1 Cache | 8KB-64KB I$ + 8KB-64KB D$ | 8KB-64KB I$ + 8KB-64KB D$
L2 Cache | 128KB - 1MB (Optional) | 128KB - 2MB (Optional)
Contrasting the Cortex-A7 and Cortex-A53 microarchitectures [75]

## Slide 244: 5.3.1 The low power Cortex-A53 (7)
We note that the Cortex-A7 has actually a partially dual-issue capability, meaning
that the second issue slot can only issue branch and integer operations.
In the Cortex-A53 the second issue slot can also issue load-store and FP/NEON
operations.
In additon, the branch prediction capabilities of the A53 were also significantly
improved by including conditional and indirect jump predictors.
Remarks [75]

## Slide 245: 5.3.1 The low power Cortex-A53 (8)
Contrasting the Cortex-A53 and Cortex-A57 arithmetic pipelines
[Based on 54]
D: Decode
R: Rename
P: Dispatch
I: Issue
E: Execute
WB: Write Back
Note: Branch and Load/Store pipelines not shown
(1x Load/Store pipeline for the Cortex A-53 and
2x Load/Store and 1x Branch pipeline for the Cortex-A-57)

## Slide 246: 5.3.1 The low power Cortex-A53 (9)
Core efficiency: 2.3 DMIPS/MHz
Expected core frequency up to 1.5 GHz.
Key features of the microarchitecture of the Cortex-A53 core -3

## Slide 247
5.3.2 The low power Cortex-A35

## Slide 248: 5.3.2 The low power Cortex-A35 (1)
5.3.2 The low power Cortex-A35 -1 (based on [12])
2012
2013
10/2009
Cortex-A5
ARMv7
40 nm
High Performance
Mainstream
Low power
Announced
1
2
3
4
5
2006
2007
2008
2009
2010
2011
10/2011
Cortex-A7
ARMv7
28 nm
10/2012
Cortex-A53
ARMv8
20/16 nm
10/2005
Cortex-A8
ARMv7
65 nm
10/2007
Cortex-A9
ARMv7
40 nm
9/2010
Cortex-A15
ARMv7
32/28 nm
10/2012
Cortex-A57
ARMv8
20/16 nm
2014
2/2014
Cortex-A17
ARMv7
28 nm
6
7
DMIPS/MHz
2015
2/2015
Cortex-A72
ARMv8
16 nm
11/2015
Cortex-A35
ARMv8
16/14 nm
8
2016
5/2016
Cortex-A73
ARMv8
10 nm
6/2013
Cortex-A12
ARMv7
28 nm

## Slide 249: 5.3.2 The low power Cortex-A35 (2)
11/2015: Announced with immediate availability for licensing.
End of 2016: First mobile devices with the Cortex-A35 expected.
It is the successor to the Cortex-A53.
It is the smallest, most efficient model of the Cortex series.
The A35 models can be used either as stand alone processors or as components
in a big-LITTLE configuration.
Target process technology: 16/14 nm.
The low power Cortex-A35 -2 [90]

## Slide 250: 5.3.2 The low power Cortex-A35 (3)
High level block diagram of the Cortex-A35 [94]
ECC: Error Correcting Code
ACP: Accelerator Coherence Port
(to connect non-cached
coherent data sources)
SCU: Snoop Control Unit
(Provides coherence within the
the processor)
AMBA: Advanced Microcontroller
Bus Architecture
(On-chip bus standard for
SoC) designs)
ACE: AXI Coherency Extensions
AMBA4 cache coherent interface
(Used in big.LITTLE systems
for smartphones, tablets,
etc.)
CHI: Coherent Hub Interface
(AMBA5 Cache coherent
interface used in servers)
AXI4: Advanced eXtensible Interface
(The most widespread AMBA4
non cache-coherent interface).

## Slide 251: 5.3.2 The low power Cortex-A35 (4)
Key features of the microarchitecture of the Cortex-A35 core -1 [90]
Fully compatible with the ARMv8 64-bit ISA.
In-order 8-stage pipeline with limited dual issue capability
Integrated L2 cache of 128 kB to 1 MB.
Up to 4 Cortex-A35 CPU cores.
Processor wide cache coherence supported by a Snoop Control Unit (SCU).
Remark
AMBA: Advanced Microcontroller Bus Architecture
(On-chip bus standard for SoC) designs
Optionally three 128-bit AMBA interfaces
AXI4: Advanced eXtensible Interface
(The most widespread AMBA4 non cache-coherent interface).
ACE: AXI Coherency Extensions
AMBA4 cache coherent interface used in big.LITTLE systems
for smartphones, tablets, etc.)
CHI: Coherent Hub Interface
(AMBA5 Cache coherent interface used in servers)

## Slide 252: 5.3.2 The low power Cortex-A35 (5)
The in-order 8-stage pipeline of the Cortex-A35 providing limited
dual issue capability Cortex-A35 [90]
ETM: Embedded Trace Macrocell, a low-level debugging technology in ARM microprocessors.
Governor: Hardware unit for setting the processor into the standby state.

## Slide 253: 5.3.2 The low power Cortex-A35 (6)
Relative performance of the Cortex-A35 vs. the Cortex-A7
assuming the same process technology (28 nm) [90]

## Slide 254: 5.3.2 The low power Cortex-A35 (7)
Relative power consumption of the Cortex-A35 vs. the Cortex-53 assuming
the same clock frequency and process technology (28 nm) [90]

## Slide 255: 5.3.2 The low power Cortex-A35 (8)
The range of configurability of the Cortex-A35 processor [90]
Configuration options of the Cortex-A35 are ranging from mobile to deeply embedded.

## Slide 256
6. Cortex-A models based on the ARMv8.2 ISA
6.3 The high performance Cortex-A75
6.4 The low power Cortex-A55
6.1 Overview
6.2 DynamIQ core clusters

## Slide 257
6.1 Overview

## Slide 258: 6.1 Overview (1)
a) Main extensions of the ARMv8 ISA-1 [97]
Revision | Released | Main enhancements | Cortex-A processors
ARMv8-A | 10/2011 |  | A32/A35/ A53/A57/ A72/A73
ARMv8.1-A | 12/2014 | Incremental benefits over v8.0 relating to the instruction set, exception model and memory translation | 
ARMv8.2-A | 03/2017 | Half-precision FP Optional increase of the address space from 48 to 52 bits RAS extensions Statistical profiling to be able to analyze large working sets | A55/A75 (Provides also ARMv8.1 support)
6.1 Overview
*

## Slide 259: 6.1 Overview (2)
Revision | Released | Main enhancements | Cortex-A processors
ARMv8.3-A | 12/2017 | Pointer authentication Improvements to the exception model for nested virtualization Small-scale enhancements to the ISA | TBA
ARMv8.4-A | 10/2018 | Cripto extensions Memory partitioning and monitoring capabilities New Secure EL2 state | TBA
ARMv8.5-A | n.a. | Vulnerability Detection Memory Tagging Branch Target Indicators Further small-scale enhancements | TBD
a) Main extensions of the ARMv8 ISA-2 [97]

## Slide 260: 6.1 Overview (3)
b) Main extensions of the microarchitecture of processors supporting
the ARMv8.2 ISA
The main extension is the DynamIQ core cluster, described in Section 6.2.

## Slide 261: 6.1 Overview (4)
ARMv8.2 ISA based processors - Overview
Source: ARM
A7x
Series
A5x
Series
A3x
Series

## Slide 262: 6.1 Overview (5)
6.3 ARM’s intention to enter the PC market
Based on SPECInt 2006 benchmark results and related estimations ARM expects
Cortex-A76-based processors to provide the same performance than Intel’s 7. gen.
(Kaby Lake based) i5-7300U processors, see Figure.
Figure: Performance comparison: ARM’s Cortex-A76 vs. Intel Core i5-7300U [99]
*

## Slide 263: 6.1 Overview (6)
ARM’s Client Compute CPU roadmap 2019-2020 [99]
*

## Slide 264: 6.1 Overview (7)
ARM’s projected performance gain for their planned processors
ARM expects faster performance gains for their planned models than awaited
for Intel’s comparable processors, as seen in the Figure below.
Figure: ARM’s projected year-over-year performance gain over Intel’s processors [100]
*

## Slide 265
6.2 DynamIQ core clusters

## Slide 266: 6.2 DynamIQ core clusters (1)
DynamIQ core clusters -2
ARM started working on the DynamIQ core cluster technology in 2013 [98].
DynamIQ was announced in 03/2017.
It is an evolution of the big.LITTLE technology, as indicated in the next slide.
*

## Slide 267: 6.2 DynamIQ core clusters (2)
6.2 DynamIQ core clusters -1
They are the next step in the evolution of the core cluster technology.
Figure: Evolution steps of the core cluster technology [114]
ARM11 MPCore (2004)
Cortex-A7/A15 (~2011)
Cortex-A55/A75 (~2017)
SMP
(
)

## Slide 268: 6.2 DynamIQ core clusters (3)
From the ARM11 MPCore to the big.LITTLE technology
CPU0
CPU1
CPU2
CPU3
Cache coherent interconnect
Cluster of
LITTLE cores
Cluster of
big cores
CPU0
CPU1
CPU2
CPU3
big.LITTLE
ARM11 MPCore [115]
(2004)
(2011)

## Slide 269: 6.2 DynamIQ core clusters (4)
CPU0
CPU1
CPU2
CPU3
Cache coherent interconnect
Cluster of
LITTLE cores
Cluster of
big cores
CPU0
CPU1
CPU2
CPU3
To
To cache coherent interconnect through the AMBA4 ACE bus
The DynamIQ technology as an evolution of the big.LITTLE technology
Two big.LITTLE core clusters
A single DynamIQ core cluster (118)
Two stand alone clusters
with up to 4 cores (2011)
A single cluster of up to8 cores of up two core types
(but up to 4 big cores) (2017)

## Slide 270: 6.2 DynamIQ core clusters (5)
DynamIQ core clusters -3
EAS (Energy Aware Scheduling).
greater flexibility with or without LITTLE cores
redesigned memory subsystem with higher bandwidth and lower access time
improved power efficiency through intelligent power management (EAS)
Benefits of the DynamIQ cluster technology:
*

## Slide 271: 6.2 DynamIQ core clusters (5b)
Remarks on EAS (Energy Aware Scheduling) [109]
Existing Linux schedulers (like the CFS (Completely Fair Scheduler)) optimize for
the throughput.
E.g. if a new task enters and there is an idle CPU the scheduler will always assign
the new task to the idle CPU.
However, this may not be the best scheduling decision for the lowest energy
consumption.
EAS is designed to optimize for lowest possible energy consumption without
affecting performance.
ARM started the development of EAS in 2015 while working with the Linux
community.

## Slide 272: 6.2 DynamIQ core clusters (5c)
DynamIQ core clusters -4
It assumes ARMv8.2 compatible cores, such as the Cortex-A55 and Cortex-A75
or Cortex-A76.
*

## Slide 273: 6.2 DynamIQ core clusters (6)
Main enhancements of DynamIQ core clusters
Up to 8 CPU cores of up to 2 ARMv8.2 ISA based core types
Private (per-core) L2 caches in the CPU cores
c) DynamIQ Shared Unit (DSU) with a shared L3 cache and snoop filter
d) Capability for partitioning the cores and the L3 cache
e) Finer-grain frequency and voltage control
f) Mesh interconnect (CMN-600) for server systems
g) Use of a scratch pad system cache to increase throughput
h) Cache stashing
(Features g) and h) will not be discussed)

## Slide 274: 6.2 DynamIQ core clusters (7)
ARMv8.2 support,
Cortex-A55/75
2 CPU types, up to 8 cores but only up to 4b/cluster
a) Up to 8 CPU cores of up to 2 ARMv8.2 ISA based core types
ARMv8.0 support,
e.g. Cortex-A53/A57/A72/A73,
single CPU type, up to 4 cores/cluster
big.LITTLE core cluster (2015) [102]
DynamIQ core cluster (2017) [118]
*
Cortex-A73 core
ARMv8.0 CPU

## Slide 275: 6.2 DynamIQ core clusters (8)
ARMv8.2 support, (Cortex-A55/75)
2 CPU types, up to 8 cores but only 4b/cluster
Private L2 caches, shared L3 cache
b) Private (per-core) L2 caches in the CPU cores
ARMv8.0 support, e.g. Cortex-A53/
A57/A72/A73, up to 4 cores/cluster
Shared L2 cache
Cortex-A73 core
ARMv8.0 CPU
big.LITTLE core cluster (2015) [55]
DynamIQ core cluster (2017) [56]
*

## Slide 276: 6.2 DynamIQ core clusters (9)
c) DynamIQ Shared Unit (DSU) with a shared L3 cache and snoop filter [106]
(Per-CPU DVFS control,
Partial L3 power down)
(Partitions)
(Up to two 128-bit AMBA 5 ACE,
256-bit AMBA 5 CHI)

## Slide 277: 6.2 DynamIQ core clusters (10)
Reduced cache latencies [106]

## Slide 278: 6.2 DynamIQ core clusters (11)
d) Capability for partitioning the cores and the L3 cache [98]
It is feasible to set up up to four partitions by assigning the cores, the external
accelerators attached to the DSU via the ACP and sections of the L3 cache
into a maximum of 4 partitions.
Partitioning may be unbalanced, e.g. 1 CPU could be assigned 2 GB whereas
the other CPUs the remaining 2 GB (assuming an 8 GB configuration).
The partitions are dynamic and can be created/adjusted during runtime by
the OS or hypervisor.
Partitioning can be useful for embedded systems that run a fixed workload or
applications that require a more deterministic runtime.

## Slide 279: 6.2 DynamIQ core clusters (12)
Example for partitioning the cores and the L3 [98]

## Slide 280: 6.2 DynamIQ core clusters (15)
e) Finer-grain frequency and voltage control [98]
Groups of CPUs (i.e. partitions)
can run at different
frequencies and voltages.
*

## Slide 281: 6.2 DynamIQ core clusters (16)
Example for two voltage and frequency domains [104]

## Slide 282: 6.2 DynamIQ core clusters (17)
f) Mesh interconnect (CMN-600) for server systems [105]

## Slide 283: 6.2 DynamIQ core clusters (18)
The reason for changing the interconnect topology for servers [105]
Ring
interconnect
Mesh
interconnect
*

## Slide 284: 6.2 DynamIQ core clusters (14)
g) Use of a scratch pad system cache to increase throughput [105]
Ingress traffic: inbound network traffic that originates from outside of the network's routers
and proceeds toward a destination inside of the network.
Egress traffic: outbound network traffic that originates inside of the network and proceeds
to another network.
It is termed also as
Agile cache.
It includes a snoop filter.

## Slide 285: 6.2 DynamIQ core clusters (13)
h) Cache stashing [98]
It enables reads/writes into the
shared L3 cache or per-core
L2 cache.
It allows closely coupled accelerators
and I/O agents to access the CPU
memory via the AMBA 5 CHI (PP) or
ACP port.
Cache stashing increases throughput.

## Slide 286: 6.2 DynamIQ core clusters (19)
Use of the mesh interconnect (CMN-600) to build a server [112]
*

## Slide 287: 6.2 DynamIQ core clusters (20)
Use of a previous ring interconnect (CCI-550) to build premium mobile
systems for 2018 [108]
CCI-550: Cache Coherent interconnect
MMU-500: Memory Management Unit (responsible for virtualization and caching)
NIC-450: Network Interconnect (interface converter)
GIC-600: General Interrupt Controller
SCP: System Control Processor
*

## Slide 288
6.3 The high performance Cortex-A75
(It won't be discussed)

## Slide 289: 6.3 The high performance Cortex-A75 (1)
6.3 The high performance Cortex-A75 -1
A7x
Series
A5x
Series
A3x
Series

## Slide 290: 6.3 The high performance Cortex-A75 (2)
05/2017: Announced along with the high-efficiency midrange Cortex-A55 and
the MALI 72 GPU.
Target process technology: 10 nm.
The high performance Cortex-A75 -2
*

## Slide 291: 6.3 The high performance Cortex-A75 (3)
The Cortex-A75 as the building block of ARM's DynamIQ core clusters [103]
Implements the ARMv8.2 ISA
Up to 8 cores (up to 4 Cortex-A75, up to 8 Cortex-A55)

## Slide 292: 6.3 The high performance Cortex-A75 (4)
STB: Store Buffer
D.E.: Default and
Exception
Block diagram of the Cortex-A75 [110]

## Slide 293: 6.3 The high performance Cortex-A75 (5)
Enhancements of the Cortex-A75 pipeline vs. the Cortex-A73 pipeline [98]
*

## Slide 294: 6.3 The high performance Cortex-A75 (6)
Innovations introduced by the NEON/FP pipelines [121], [98]

## Slide 295: 6.3 The high performance Cortex-A75 (7)
Per-core performance and efficiency of the Cortex-A75 [98]

## Slide 296: 6.3 The high performance Cortex-A75 (8)
Contrasting the performance of the Cortex-A75 vs. the Cortex-A73 [106]

## Slide 297
6.4 The high performance Cortex-A76

## Slide 298: 6.3 The high performance Cortex-A75 (1)
6.4 The high performance Cortex-A76 -1
A7x
Series
A5x
Series
A3x
Series
Source: AMD

## Slide 299: 6.4 The high performance Cortex-A76 (1)
Main design goals
Laptop-class performance with mobile efficiency while outperforming the competition at half by silicon area and power consumption.
To achieve this
remove bottlenecks throughout the design to improve performance
optimize every microarchitectural feature to extract maximal performance
at minimal power and area
brand new, wider microarchitecture vs. the preceding ones
Enhanced, 2. gen. DynamIQ core cluster.
Targeting 12, 7 or 5 nm process technology.
The Cortex-A76 can be combined with the Cortex-A55 CPU.
The high performance Cortex-A76 -2

## Slide 300: 6.4 The high performance Cortex-A76 (2)
Performance and power efficiency improvements of the Cortex-A76 [119]
Figure: Performance and power efficiency of a 3.0 GHz 7 nm Cortex-A76 vs. a 2.8 GHz 10 nm Cortex-A75 []

## Slide 301: 6.4 The high performance Cortex-A76 (3)
MLP: Memory Level Parallelism
Overview of the microarchitecture of the Cortex-A76 [119]
ASIMD (Advanced SIMD): FMAD etc. operations are executed interleaved (called with late
forwarding) i.e. FMAD operations will already be started when the multiply operands are
available and the accumulate operand will be added later after the multiply operation has
already been calculated in order to speed up the execution of a chain of FMAD etc. instructions.

## Slide 302: 6.4 The high performance Cortex-A76 (4)
Key enhancements of the microarchitecture
4-wide front-end, up from 3 of the previous Cortex-A75
dispatch rate of 8, up from 6 in the previous Cortex-A75
larger issue buffers

## Slide 303: 6.4 The high performance Cortex-A76 (5)
4-wide front-end (up from 3 in the previous Cortex-A75) [119]

## Slide 304: 6.4 The high performance Cortex-A76 (6)
MLP: Memory Level Parallelism
Dispatch rate of 8 (up from 6 in the previous Cortex-A75) to 8) [119]

## Slide 305: 6.4 The high performance Cortex-A76 (7)
MLP: Memory Level Parallelism
Larger issue buffers (IsQ/IQ) [119]
Note that the issue queues of the Cortex-A76 typically have 16 entries rather than 12 seen
in the Cortex-A75.

## Slide 306: 6.4 The high performance Cortex-A76 (8)
The cache hierarchy of the Cortex-A76 processor [119]

## Slide 307: 6.4 The high performance Cortex-A76 (9)
Bandwidth improvements of A76’s caches vs. the A75 caches [119]

## Slide 308: 6.4 The high performance Cortex-A76 (10)
Performance improvements in subsequent high-performance Cortex-A
processors [119]
GEMM lowp is a library for multiplying matrices of 8-bit integers (used in NN apps.)

## Slide 309: 6.4 The high performance Cortex-A76 (11)
Performance improvements claims over the Cortex-A75 processors [119]
Single-thread performance improvements
+25% more integer IPC than the Cortex-A75 CPU
+35 % higher ASIMD/FP performance
Mobile usage performance improvements
+28% more Geekbench performance
+35 % more Javaacript performance
Performance improvements while using AI applications
3.9x higher AI performance

## Slide 310: 6.4 The high performance Cortex-A76 (12)
Single core performance of competing processors for Geekbench 4 [119]

## Slide 311: 6.4 The high performance Cortex-A76 (13)
System architecture of a Cortex-A76 based mobile system [120]

## Slide 312
6.4 The high efficiency Cortex-A55
(It won't be discussed)

## Slide 313: 6.4 The high efficiency Cortex-A55 (1)
6.4 The high efficiency Cortex-A55 -1
Source: AMD
A7x
Series
A5x
Series
A3x
Series
Source: AMD

## Slide 314: 6.4 The high efficiency Cortex-A55 (2)
05/2017: Announced along with the high-performance Cortex-A75 and
the MALI 72 GPU.
Target process technology: 10 nm.
The high efficiency Cortex-A55 -2
*

## Slide 315: 6.4 The high efficiency Cortex-A55 (3)
The Cortex-A55 as the building block of ARM's DynamIQ core clusters [103]
Implements the ARMv8.2 ISA
Up to 8 cores (up to 4 Cortex-A75, up to 8 Cortex-A55)

## Slide 316: 6.4 The high efficiency Cortex-A55 (4)
Enhancements of the Cortex-A55 vs. the Cortex-A53 [98]

## Slide 317: 6.4 The high efficiency Cortex-A55 (5)
Contrasting the performance of the Cortex-A55 vs. the Cortex-A53 [106]

## Slide 318
7. Overview of ARM’s Mali graphics series
Will not be discussed.

## Slide 319: 7. Overview or ARM’s Mali graphics series (1)
7. Overview of ARM’s Mali graphics series (since 2010)
Performance oriented
graphics series
ARM Mali graphics series (since 2010)
Cost efficient
graphics series
ARM also designs and licenses GPUs to be used as companion chips to their CPU
chips.
ARM’s GPU lines are designated as Mali graphics series.

## Slide 320: 7. Overview of ARM’s Mali graphics lines (2)
Overview of ARM’s Mali graphics seeries
Only GPU parts announced since about 2010 will be discussed [20]
Performance oriented
graphics series
Mali-T6xx - Mali-T8xx
Cost efficient
graphics series
Mali-T4xx - Mali-T8xx

## Slide 321: 7. Overview of ARM’s Mali graphics lines (3)7
ARM’s performance oriented Mali graphics series [20]

## Slide 322: 7. Overview of ARM’s Mali graphics lines (4)
ARM’s cost efficient Mali graphics series [20]

## Slide 323: 7. Overview of ARM’s Mali graphics lines (5)
ARM’s high-end GPU roadmap [51]
Companion GPU to A57 (announced 10/2013)

## Slide 324
8. References

## Slide 325
8. References (1)
[2]: Shimpi A.L., Answered by the Experts: ARM's Cortex A53 Lead Architect, Peter Greenhalgh,
AnandTech, Dec. 17 2013, http://www.anandtech.com/show/7591/answered-by-the-
experts-arms-cortex-a53-lead-architect-peter-greenhalgh
[3]: Hill S., Design of a Reusable 1GHz, Superscalar ARM Processor, Hot Chips-18, Aug. 22 2006,
http://www.hotchips.org/wp-content/uploads/hc_archives/hc18/3_Tues/HC18.S6/HC18.S6T3.
pdf
[1]: Architecture and Implementation of the ARM Cortex-A8 Microprocessor, Design & Reuse,
http://www.design-reuse.com/articles/11580/architecture-and-implementation-of-the-
arm-cortex-a8-microprocessor.html
[4]: Details of a New Cortex Processor Revealed, Cortex-A9, ARM Developers’ Conference,
Oct. 2007, http://rtcgroup.com/arm/2007/presentations/174%20-%20Details%20of%
20a%20New%20Cortex%20Processor%20Revealed%20Cortex-A9.pdf
[5]: ARM Teaching Material, http://www.arm.com/files/ppt/ARM_Teaching_Material.ppt
[6]: ARM Cortex Application Processors, http://www.arm.com/products/processors/index.php
[7]: ARM SecurCore Processors, http://www.arm.com/products/processors/securcore/index.php
[8]: Snyder C.D., ARM Family Expands at EPF, ARM11 Microarchitecture Stretches Pipe to Boost
Frequency, Microprocessor, June 3 2002
[9]: Hirata K., ARM11 MPCore, The streamlined and scalable ARM11 processor core, Jan. 2007,
http://www.aspdac.com/aspdac2007/pdf/archive/7D-2.pdf

## Slide 326
[11]: NEON, ARM Technologies,
http://www.arm.com/products/processors/technologies/neon.php
[12]: Goodacre J., The Evolution of the ARM Architecture Towards Big Data and the Data-Centre,
8th Workshop on Virtualization in High-Performance Cloud Computing (VHPC’13),
Nov. 17-22 2013, http://www.virtical.eu/pub/sc13.pdf
[10]: ARM Introduces The Cortex-M3 Processor To Deliver High Performance In Low-Cost
Applications, Oct. 19 2004, http://www.arm.com/about/newsroom/6750.php
[13]: Ferguson I., Redefining User Experiences, from IoT to Smart Mobile Devices, June 14 2013,
http://www.arm.com/zh/files/event/arm_multimedia_seminar_shenzhen_2013_ianferguson.
pdf
[14]: Goto H., ARM Cortex – A Family Architecture, 2010,
http://pc.watch.impress.co.jp/video/pcw/docs/423/409/p1.pdf
[15]: Stevens H., Introduction to AMBA 4 ACE and big.LITTLE Processing Technology, White Paper,
June 6 2011, http://www.arm.com/files/pdf/CacheCoherencyWhitepaper_6June2011.pdf
[16]: Shimpi A.L., The ARM Diaries, Part 2: Understanding the Cortex A12, AnandTech,
July 17 2013, http://www.anandtech.com/show/7126/the-arm-diaries-part-2-
understanding-the-cortex-a12
[17]: Shimpi A.L., ARM Cortex A17: An Evolved Cortex A12 for the Mainstream in 2015,
AnandTech, Febr. 11 2014, http://www.anandtech.com/show/7739/arm-cortex-a17
[18]: Ryan H., Intel, AMD & ARM Processors, University of Wisconsin DoIT Techstore
https://kb.wisc.edu/showroom/page.php?id=4927
8. References (2)

## Slide 327
[20]: Mali Performance Efficient Graphics, ARM
http://www.arm.com/products/multimedia/mali-performance-efficient-graphics/index.php
[21]: Cortex-A8 Processor, ARM Cortex-A Series,
http://www.arm.com/products/processors/cortex-a/cortex-a8.php
[19]: Rao A., ARM: a mandatory primer, Element14, 2014
[22]: Architecture and Implementation of the ARM Cortex-A8 Microprocessor, White Paper,
Oct. 2005, https://www.pixhawk.ethz.ch/_media/software/optimization/neon_whitepaper.pdf
[23]: Shimpi A.L., Understanding the iPhone 3GS, AnandTech, July 7 2009,
http://www.anandtech.com/print/2798/
[24]: The ARM Cortex-A9 Processors, White Paper, Sept. 2009,
http://www.arm.com/files/pdf/armcortexa-9processors.pdf
[25]: Cortex-A9 MPCore, Technical Reference Manual, 2008-2012,
http://infocenter.arm.com/help/topic/com.arm.doc.ddi0407i/DDI0407I_cortex_a9_
mpcore_r4p1_trm.pdf
[26]: Goto H., ARM Cortex-A9r4 Core Block Diagram,
http://pc.watch.impress.co.jp/video/pcw/docs/614/543/08p.pdf
[27]: ARM Unveils Cortex-A9 Processors For Scalable Performance and Low-Power Designs,
Oct. 3 2007, http://www.arm.com/about/newsroom/18688.php
[28]: Goodacre J., The Effect and Technique of System Coherence in ARM Multicore Technology,
http://www.mpsoc-forum.org/previous/2008/slides/8-6%20Goodacre.pdf
8. References (3)

## Slide 328
[30]: Goto H., ARM Cortex-A12 Block Diagram, 2013,
http://pc.watch.impress.co.jp/video/pcw/docs/621/747/gp1.pdf
[29]: Goto H., ARM Cortex-A7/A9 vs Bobcat, Atom, 2010,
http://pc.watch.impress.co.jp/img/pcw/docs/487/030/html/9.jpg.html
[31]: Rosinger S., The Top 5 Things to Know about Cortex-A12, ARM Connected Community,
Oct. 26 2013, http://community.arm.com/groups/processors/blog/2013/10/26/the-top-5-
things-to-know-about-cortex-a12
[32]: ARM Cortex-A17 MPCore Processor, Technical Reference Manual, 2014,
http://infocenter.arm.com/help/topic/com.arm.doc.ddi0535b/DDI0535B_cortex_a17_
r1p0_trm.pdf
[33]: Cortex-A17 Processor, ARM Cortex-A Series,
http://www.arm.com/products/processors/cortex-a/cortex-a17-processor.php
[34]: Rosinger S., ARM Cortex-A17/Cortex-A12 processor update, ARM Connected Community,
Oct. 1 2014, http://community.arm.com/groups/processors/blog/2014/09/30/arm-
cortex-a17-cortex-a12-processor-update
[35]: Cortex-A15 Processor, ARM Cortex-A Series,
http://www.arm.com/products/processors/cortex-a/cortex-a15.php
[36]: Lanier T., Exploring the Design of the Cortex-A15 Processor,
http://www.arm.com/files/pdf/AT-Exploring_the_Design_of_the_Cortex-A15.pdf
8. References (4)

## Slide 329
[38]: Stokes J., ARM fills out CPU lineup with Cortex A5, Ars Technica, Oct. 22 2009,
http://arstechnica.com/gadgets/2009/10/arm-fills-out-cpu-lineup-with-cortex-a5/
[37]: Greenhalgh P., big.LITTLE Processing with ARM Cortex-A15 & Cortex-A7, White Paper,
Sept. 2011, http://www.arm.com/files/downloads/big_LITTLE_Final_Final.pdf
[39]: Hruska J., ARM Launches New Cortex-A5 As A Bulkward Against Future Atom processors,
Hot Hardware, Oct. 23 2009, http://hothardware.com/News/ARM-Launches-New-
CortexA5-As-A-Bulkward-Against-Future-Atom-processors
[40]: Cortex-A5 Processor, ARM Cortex-A Series,
http://www.arm.com/products/processors/cortex-a/cortex-a5.php
[41]: Bhattacharya A., Small, Quiet, and Cool, Power Efficient Processing with the Cortex-A5
Processor, http://www.arm.com/files/pdf/at2_-_power_efficient_processing_with_the_
cortex-a5_v1.pdf
[42]: Cortex-A5, The smallest, lowest power ARMv7 application processor,
http://www.hitex.co.uk/fileadmin/uk-files/pdf/ARM%20Seminar%20Presentations%
202013/Hitex%20Cortex-A5%20Overview.pdf
[43]: Flautner K., Heterogeneity to the rescue, Nov. 2011,
https://www.bscmsrc.eu/sites/default/files/media/arm-heterogenous-mp-november-2011.
pdf
[44]: Shimpi A.L., ARM's Cortex A7: Bringing Cheaper Dual-Core & More Power Efficient High-End
Devices, AnandTech, Oct. 19 2011, http://www.anandtech.com/show/4991/
8. References (5)

## Slide 330
[46]: Goto H., New design of mid-range CPU that ARM has announced "Cortex-A12", PC Watch,
June 4 2013, http://pc.watch.impress.co.jp/docs/column/kaigai/20130604_602106.html
[45]: Cortex-A7 Processor, ARM Cortex-A Series,
http://www.arm.com/products/processors/cortex-a/cortex-a7.php
[47]: Shimpi A.L., ARM's Cortex A57 and Cortex A53: The First 64-bit ARMv8 CPU Cores,
AnandTech, Oct. 30 2012, http://www.anandtech.com/show/6420/arms-cortex-a57-
and-cortex-a53-the-first-64bit-armv8-cpu-cores
[48]: Smith K., Next-Generation Solutions: One Size Does Not Fit All, Nov. 2012,
http://www.armtechforum.com.cn/2012/3_Next-generation_Solutions_One_Size_does_
not_Fit_All.pdf
[49]: Smythe I., Building the future of 64-bit computing with ARMv8-A, June 2014,
http://www.arm.com/files/event/2014_ARM_Multimedia_Seminar_ARM_Ian_Smythe.pdf
[50]: Ferguson I., ARM Servers, Why, Where, when, Nov. 27 2012,
http://openserversummit.com/English/Collaterals/Proceedings/2012/20121127_SA103_
Ferguson.pdf
[51]: Crijns K., ARM: 20 dollar and 64-bit Android smartphones to be expected, Hardware.info,
June 24 2014, http://us.hardware.info/reviews/5386/2/arm-20-dollar-and-64-bit-android-
smartphones-to-be-expected-android-64-bitn
[52]: Scaling Mobile Compute to the Data Centre, MPSoC’13,
http://www.mpsoc-forum.org/previous/2013/slides/2-Goodacre.pdf
8. References (6)

## Slide 331
[54]: Mandyam L., Smartphone Powered Data Centers: Shifting Toward Energy Efficiency,
http://sites.ieee.org/scv-cs/files/2013/03/IEEE-event-April-slide-upload.pdf
[53]: ARM Launches Cortex-A50 Series, the World's Most Energy-Efficient 64-bit Processors,
TechPowerUp, Oct. 30 2012, http://www.techpowerup.com/174709/arm-launches-cortex-
a50-series-the-worlds-most-energy-efficient-64-bit-processors.html
[55]: Anthony S., ARM says $20 smartphones coming this year, shows off 64-bit Cortex-A53 and
A57 performance, Extreme Tech, May 6 2014, http://www.extremetech.com/computing/
181935-arm-says-20-smartphones-coming-this-year-shows-off-64-bit-cortex-a53-and-
a57-performance
[56]: Merritt R., ARM stretches out with A5 core, graphics, FPGAs, Oct. 21 2009,
http://www.embedded.com/print/4085371
[57]: Cormie D., The ARM11 Microarchitecture, April 2002
[58]: Exynos 5 Octa, Block Diagram,
http://www.samsung.com/global/business/semiconductor/product/application/detail?
productId=7978&iaId=2341
[59]: Grabham D., From a small Acorn to 37 billion chips: ARM's ascent to tech superpower,
Techradar, July 19 2013, http://www.techradar.com/news/computing/from-a-small-acorn-
to-37-billion-chips-arm-s-ascent-to-tech-superpower-1167034
[60]: The ARM Architecture, http://www.eng.auburn.edu/~strouce/DaTseminar/UniPres07s.pdf
[61]: Wikipedia, ARM architecture, http://en.wikipedia.org/wiki/ARM_architecture
8. References (7)

## Slide 332
[63]: Lemieux J., Introduction to ARM thumb, Embedded, Sept. 24 2003, http://www.embedded.
com/electronics-blogs/beginner-s-corner/4024632/Introduction-to-ARM-thumb
[62]: Levy M., The History of The ARM Architecture: From Inception to IPO,
http://www.reds.ch/share/cours/ReCo/documents/TheHistoryOfTheArmArchitecture.pdf
[64]: ARM Processor Architecture,
http://www.arm.com/products/processors/instruction-set-architectures/index.php
[65]: ARM Architecture Reference Manual, ARMv5, DDI0100E, June 2000
[66]: ARM Architecture Reference Manual, ARMv8, 2013, http://www.myir-tech.com/down/arm/
arch/ARMv8-A_Architecture_Reference_Manual_%28Issue_A.a%29.pdf
[67]: Porthouse C., Use ARM DBX hardware extensions to accelerate Java in space-constrained
embedded apps, Embedded, Oct. 18 2007, http://www.embedded.com/design/prototyping-
and-development/4007206/3/PRODUCT-HOW-TO-Use-ARM-DBX-hardware-extensions-to-
accelerate-Java-in-space-constrained-embedded-apps
[68]: ARM Security Technology, Building a Secure System using TrustZone Technology, 2009,
http://infocenter.arm.com/help/topic/com.arm.doc.prd29-genc-009492c/PRD29-GENC-
009492C_trustzone_security_whitepaper.pdf
[69]: ARM Cortex-A53 MPCore Processor Technical Reference Manual, Cryptography Extension,
2013-2014, http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.ddi0500e/
CJHDEBAF.html
8. References (8)

## Slide 333
[70]: Shilov A., ARM’s high-end ‘Ares’ core for 10nm SoCs may be unveiled next year, KitGuru,
May 16 2015, http://www.kitguru.net/components/cpu/anton-shilov/arms-high-
performance-ares-core-may-be-unleashed-next-year/
[71]: Goto H., ARM Cortex-A57 Block Diagram,
http://images.anandtech.com/doci/8718/Hiroshige.Goto.png
[72]: Wasson S., Inside ARM's Cortex-A72 microarchitecture, TechReport, May 1 2015,
http://techreport.com/review/28189/inside-arm-cortex-a72-microarchitecture
[73]: Citizendium, Java platform, http://en.citizendium.org/wiki/Java_platform
[74]: Wasson S., Samsung's Galaxy Note 4 with the Exynos 5433 processor, TechReport,
01/31/2015, http://techreport.com/review/27539/samsung-galaxy-note-4-with-the-
exynos-5433-processor/2
[75]: Frumusanu A. & Smith R., ARM A53/A57/T760 investigated - Samsung Galaxy Note 4
Exynos Review, AnandTech, February 10, 2015,
http://www.anandtech.com/show/8718/the-samsung-galaxy-note-4-exynos-review
[76]: Riemenschneider F., Intel sei dank: Programmierbare Logik mit 1 GHz takten,
Elektroniknet, 29.10.2013 von Frank Riemenschneider,
http://www.elektroniknet.de/halbleiter/programmierbare-logik/artikel/102160/
[77]: Frumusamu A., ARM Announces New Cortex-A35 CPU - Ultra-High Efficiency For Wearables
& More, AnandTech, November 10, 2015,
http://anandtech.com/show/9769/arm-announces-cortex-a35
8. References (9)

## Slide 334
[78]: Quested T., ARM scales up again in Cambridge, Businessweekly, 20 October, 2014,
http://www.businessweekly.co.uk/news/property-and-construction/17695-arm-scales-
again-cambridge#sthash.Pzg7jnpK.dpuf
[79]: ARM Architecture Reference Manual, Thumb-2 Supplement, 2004-2005,
http://read.pudn.com/downloads159/doc/709030/Thumb-2SupplementReferenceManual.pdf
[80]: Wanted: Java bytecode disassembler that shows addresses, opcodes, operands, in hex,
Reverse Engineering, 2013, http://reverseengineering.stackexchange.com/questions/
2036/wanted-java-bytecode-disassembler-that-shows-addresses-opcodes-operands-in-h
[81]: Barr M., KVM: A Small Java Virtual Machine for J2ME, Barr Group, May 4 2016,
http://www.barrgroup.com/Embedded-Systems/How-To/KVM-J2ME-Java-Virtual-Machine
[82]: What is Bytecode ?, March 21 2015,
http://interview-question-and-answers.blogspot.hu/2015/03/what-is-bytecode.html
[83]: The JVM – Java Virtual Machine, Android Developer, May 8 2015,
http://androiddeveloper.co.il/the-jvm-java-virtual-machine/
[84]: Java Virtual Machine, Free Download Java Virtual Machine, How to Download JVM,
Dev Manuals, Sept. 28 2010,
http://www.devmanuals.com/tutorials/java/corejava/javavirtualmachine.html
[85]: Srinivasan K., What is the difference between JRE,JVM and JDK?, Javabeat, Febr. 21 2013,
http://www.javabeat.net/what-is-the-difference-between-jrejvm-and-jdk/
8. References (10)

## Slide 335
[86]: ARM Architecture Reference Manual, ARMv7-A and ARMv7-R edition, 2004-2012,
http://liris.cnrs.fr/~mmrissa/lib/exe/fetch.php?media=armv7-a-r-manual.pdf
[87]: Cortex-A7 MPCore, Technical Reference Manual, Rev. r0p3, 2011-2012,
http://infocenter.arm.com/help/topic/com.arm.doc.ddi0464d/DDI0464D_cortex_a7_
mpcore_r0p3_trm.pdf
[88]: Pardoe A., New Innovations in .NET Runtime, dotnetConf, 2014, Jun. 2014,
https://view.officeapps.live.com/op/view.aspx?src=http%3a%2f%2ffiles.channel9.
msdn.com%2fthumbnail%2f47cb5ae5-eb38-404d-80e8-7bae0a4efbaf.pptx
[89]: Cortex-A73 Processor, ARM,
https://www.arm.com/products/processors/cortex-a/cortex-a73-processor.php
[90]: Frumusanu A., ARM Announces New Cortex-A35 CPU - Ultra-High Efficiency For Wearables
& More, AnandTech, Nov. 10, 2015,
http://www.anandtech.com/show/9769/arm-announces-cortex-a35
[91]: Frumusanu A., ARM Reveals Cotex-A72 Architecture Details, AnandTech, Apr. 23, 2015,
http://www.anandtech.com/show/9184/arm-reveals-cortex-a72-architecture-details
[92]: Frumusanu A., The ARM Cortex A73 - Artemis Unveiled, AnandTech, May 29, 2016,
http://www.anandtech.com/show/10347/arm-cortex-a73-artemis-unveiled
[93]: Cortex-A73 Overview, ARM Developer, 2016,
https://developer.arm.com/products/processors/cortex-a/cortex-a73
[94]: Cortex-A35, ARM, 2015,
http://www.arm.com/products/processors/cortex-a/cortex-a35-processor.php
8. References (11)

## Slide 336
[95]: Wasson S., Inside ARM's Cortex-A72 microarchitecture - The next-gen CPU core for mobile
devices and servers, Tech Report, May 1, 2015,
http://techreport.com/review/28189/inside-arm-cortex-a72-microarchitecture
[96]: Stephens N., ARMv8-A Next-Generation Vector Architecture for HPC, Hot Chips 2016,
https://community.arm.com/groups/processors/blog/2016/08/22/technology-update-
the-scalable-vector-extension-sve-for-the-armv8-a-architecture
[97]: Brash D., The ARMv8-A architecture and its ongoing development, ARM, 2014
https://community.arm.com/processors/b/blog/posts/the-armv8-a-architecture-and-its-
ongoing-development
[98]: Humrick M., Exploring DynamIQ and ARM’s New CPUs: Cortex-A75, Cortex-A55,
AnandTech, May 29, 2017,
https://www.anandtech.com/show/11441/dynamiq-and-arms-new-cpus-cortex-a75-a55
[99]: Frumusanu A., The ARM Cortex A73 - Artemis Unveiled, AnandTech, May 29, 2016,
http://www.anandtech.com/show/10347/arm-cortex-a73-artemis-unveiled
[100]: Turner C., ARM instruction sets and CPUs for wide ranging applications, ARM Tech Forum,
Taipei, July 4, 2017,
https://www.arm.com/files/event/20170704_ATF_TW_A3.pdf
[101]:Cortex-A75, ARM Developer,
https://developer.arm.com/products/processors/cortex-a/cortex-a75
[102]: Cortex-A73, ARM Developer,
https://developer.arm.com/products/processors/cortex-a/cortex-a73
8. References (12)

## Slide 337
[103]: ARM Unveils Cortex-A75, A55 Processors And Mali-G72 GPU, ARM Developer,
https://www.xda-developers.com/arm-unveils-cortex-a75-a55-processors-and-mali-
g72-gpu/
[104]: DynamIQ power management support, Vers. 1.1, ARM ECM 0640541 Oct. 30 2017
[105]: Parris N., Boost SoC performance from edge to cloud ARM CoreLink System IP, ARM,
Nov. 2016,
http://www.armtechforum.com.cn/attached/article/2016ATS_C1_Neil_Parris
20161206151154.pdf
[106]: Greenhalgh P., ARM DynamIQ. Intelligent Solutions Using Cluster Based Multiprocessing,
Hot Chips 29, 2017 Aug. 12,
https://www.slideshare.net/ARMHoldings/arm-dynamiq-intelligent-solutions-using-
cluster-based-multiprocessing
[107]: Wathan G. : Arm DynamIQ: Technology for the next era of compute, ARM Community,
https://community.arm.com/processors/b/blog/posts/arm-dynamiq-technology-for-
the-next-era-of-compute
[108]: Walrath J., ARM Tech Day 2017: DynamIQ, Cortex-A55, A75, and Mali-G72,
PC Perspective, May 29, 2017,
https://www.pcper.com/reviews/General-Tech/ARM-Tech-Day-2017-DynamIQ-
Cortex-A55-A75-and-Mali-G72/Cortex-A75-and-Mali-G72
[109]: Rickards I. and Kucheria A., Energy Aware Scheduling (EAS) progress update, Linaro
Company, Sept. 18, 2015,
http://www.linaro.org/blog/core-dump/energy-aware-scheduling-eas-progress-update/
8. References (13)

## Slide 338
[110]: Triggs R., A closer look at ARM’s new Cortex-A75 and Cortex-A55 CPUs, Android Authority,
May 31, 2017
https://www.androidauthority.com/arm-cortex-a75-cortex-a55-breakdown-770380/
[111]: Arm Cortex-A55: Efficient performance from edge to cloud, ARM Community,
https://community.arm.com/processors/b/blog/posts/arm-cortex-a55-efficient-
performance-from-edge-to-cloud
[112]: System Guidance for Infrastructure, ARM Developer,
https://developer.arm.com/products/system-design/system-guidance/system-guidance-
for-infrastructure
[113]: ARM® Architecture Reference Manual ARMv8, for ARMv8-A architecture profile,
ARM DDI 0487A.k_iss10775 (ID092916),2013-2016
https://silver.arm.com/download/ARM_and_AMBA_Architecture/AR150-DA-70000-r0p0-
01eac1/DDI0487A_k_armv8_arm_iss10775.pdf
[114]: Arm DynamIQ: Technology for the next era of compute, ARM Community,
https://community.arm.com/processors/b/blog/posts/arm-dynamiq-technology-for-the-
next-era-of-compute
[115]: ARM unveils multi-processor core with Linux SMP support, LinuxDevices, May 17, 2004,
http://linuxdevices.linuxgizmos.com/arm-unveils-multi-processor-core-with-linux-smp-
support/
[116]: ARM Architecture Reference manual Supplement - The Scalable Vector Extension (SVE),
for ARMv8-A, ARM DDI 0584Ab (ID081717), 21 Aug. 2017,
https://developer.arm.com/docs/ddi0584/latest/arm-architecture-reference-manual-
supplement-the-scalable-vector-extension-sve-for-armv8-a
8. References (14)

## Slide 339
[117]: ARM Q4 2016 Roadshow Slides, ARM Holdings, 2017
file:///C:/Users/sima/Downloads/ARM_SB_Q4_2016_Roadshow_Slides_FINAL.pdf
8. References (15)
[118]: Triggs R., Everything you need to know about ARM’s DynamIQ, Android Authority,
May 29, 2017,
https://www.androidauthority.com/arm-dynamiq-need-to-know-770349/
[119]: Frumusanu A., Arm's Cortex-A76 CPU Unveiled: Taking Aim at the Top for 7nm,
AnandTech, May 31, 2018,
https://www.anandtech.com/show/12785/arm-cortex-a76-cpu-unveiled-7nm-powerhouse
[120]: Hruska J., ARM’s New Cortex-A76 SoC Targets Windows Laptop Market, ExtremeTech,
May 31, 2018,
https://www.extremetech.com/mobile/270362-arm-cortex-a76-targets-laptop-market
[121]: Humrick M., Exploring DynamIQ and ARM’s New CPUs: Cortex-A75, Cortex-A55,
AnandTech, May 29, 2017,
https://www.anandtech.com/show/11441/dynamiq-and-arms-new-cpus-cortex-a75-
a55/3
[122]: Cortex-A57 Software Optimization Guide, ARM, UAN 0015B, 2016,
http://infocenter.arm.com/help/topic/com.arm.doc.uan0015b/Cortex_A57_Software_
Optimization_Guide_external.pdf
[123]: ASIMD multiply-accumulate instruction, ARM Community, 2016,
https://community.arm.com/processors/f/discussions/7028/asimd-multiply-accumulate-
instruction

## Slide 340
[124]: Gianos C., Intel Xeon Processor E5-2600 v3 Product Family Architectural Overview ,
HPCC'14, Nov. 16 2014